## Introduction

This guide documents the specifications for submitting data for the Unregulated Contaminant Monitoring Regulation (UCMR) program to the U.S. Environmental Protection Agency (EPA) using Extensible Markup Language (XML) standards. Only laboratories that are registered with EPA’s Central Data Exchange (CDX) can submit data to the Safe Drinking Water Accession and Review System (SDWARS), the information system that supports the collection of data for the UCMR.

Preliminary analytical data are entered by laboratories on behalf of the public water systems (PWSs) participating under the rule. The PWS can then review their data online. Data approved by the PWS are then available for state and EPA review before being transmitted to the National Drinking Water Contaminant Occurrence Database (NCOD). To learn more about CDX and how to register, contact the CDX Helpdesk by phone (1-888-890-1995) or by e-mail at EPACDX@CSC.COM.

## Error Corrections and Resubmissions

Correcting Errors

If a submission contains errors that prevent it from being parsed into SDWARS, CDX will notify you of the error by sending a notification to your “MyCDX” inbox (see Figure 1) and your registered e-mail address.

Figure 1. CDX Inbox with Error Notification

Data checks occur at two stages during the file upload process—authentication and data validation. Authentication occurs as soon as CDX receives the file. CDX authenticates your account and the file name. These messages are sent to your “MyCDX” inbox and your e-mail address registered with CDX. Table 1 shows the error messages you could receive.

Table 1. Authentication Error Messages

Error Message

TBD

The data validation function performs checks by the parser and additional checks in two parts—format and UCMR validations. There are two different error messages for XML—parsing errors and data validation errors. CDX will parse the file. If the file is not valid and well-formed, CDX will provide a text file listing the parsing errors (see Figure 2). This file is sent to your “MyCDX” inbox. While a copy of the error notification will be sent to your registered e-mail address, you can only view the list of errors through the error notice in your “MyCDX” inbox. The parsing error messages are generic messages. If 50 errors are found, CDX stops parsing the file and sends the error message, noting that the file may contain additional errors.

Figure 2. Error Message from Parser

TBD

If the file is valid and well-formed, CDX will conduct data validation and verifications according to UCMR. If the file does not pass the checks, CDX will provide an error message to your “MyCDX” inbox. Here too, a copy of the notification will be sent to your e-mail address directing you to view the error details online.

The message (see Figure 3) is numbered and provides an explanation, the extract of the record that contains the error, and an administrator message. The administrator message is applied to assist technical support when typical solutions do not work. The technical support staff may request the associated administrator message to assist them and the programmers in identifying a solution to an error. The text file lists up to the first 50 errors in the submitted file. Message number one of Figure 3 does not include an administrator message while message number two does.

SDWARS verifies the data by first checking general format and verifies IDs (i.e., correct format for date, valid PWS ID, valid method, valid facility ID, valid sample point ID). Table 2 lists common error messages for data formatting and general validations. These messages identify the probable cause for the error.

Figure 3. Text File with Details of Errors

TBD

Table 2. Common Formatting/Validation Error Messages

Error message

analytical result is already on record

analytical result is not on record

facility identifier is not five digits

facility is not on record

lab is not on record

PWS is not on record

sample collection date postdates sampling event data entry

sample collection date predates publication of the final rule

sample collection date predates the start of monitoring

sampling event is not on record

sampling point identifier contains non-letter, non-digit characters

sampling point is not on record

sampling schedule is not on record

user identifier is not formatted correctly

Resubmitting Data

A file containing only original data or including original and replacement data can be submitted. The analyte results data may be replaced only if the existing results have not been approved. When resubmitting replacement data, you must use the code “r” in the TransactionPurposeIdentifier element. The “r” indicates the transaction contains records that will replace existing records. The resubmission will overwrite the existing data in the SDWARS database. You may confirm that the data was overwritten by viewing the records in the SDWARS Web application.

Users from your laboratory are the only users that may edit your sampling and analytical data. You can only edit data that is in “lab hold” status in the SDWARS database. If you need to edit data that it has already been approved, you can contact the PWS to return the control of the record back to your lab for corrections. If the record was also approved by the PWS, then the PWS must request that the SDWARS database administrator/Workbook Manager return editing rights to your laboratory. The SDWARS database administrator/Workbook Manager can be contacted through CDX Technical Support.

Checking the Range of Data Values

In addition to the edit validations described in the preceding sections, SDWARS reviews several fields for specific values or ranges. In some cases it may entirely reject the record for failing the range check, while in others it may create a warning that requires the laboratory to manually review and either approve or modify the results. This section describes each of these fields.

UCMR Data Range Checks - ?????????????????????

The UCMR has specific minimum values for different analytes. Information about minimum reporting levels (MRLs) is in the following regulation:

- 40 CFR, Part 141, “Monitoring requirements for the unregulated contaminants;” final rule, January 4, 2007

SDWARS Data Range Checks

SDWARS will check the range of some data values. Table 4 shows the list of elements that SDWARS checks. SDWARS assigns a range or value that the element must satisfy, and the range or value it should satisfy. The “must” checks will prevent the data from loading and will result in an error notification to your “MyCDX” inbox and registered e-mail address. However, the “should” checks will not result in preventing the data from loading. Instead, the “should” checks will flag results as having potential errors for your laboratory to confirm. If data are submitted that violate the “should” criteria, then the status of those records will be “lab hold” and you must use the Web forms to override the range check (or correct the value through Web forms or a replacement file). You cannot approve data where a range check notification has not been addressed. Thus, the data cannot be sent to the PWS to approve and will remain in the “lab hold” status.

You have two options to edit a range check. In order to override the warning message and approve the data, you must use the Web forms. If, in reviewing the data, you believe the data should be corrected, you may do so either by using the Web form or by correcting the data in your system and issuing a replacement transaction.

Table 4. Range Checks Performed by SDWARS

| Error | Can be overridden? |
| --- | --- |
| concentration fortified result value is less than one half of the minimum reporting level | N |
| concentration fortified result value is more than the maximum reasonable value | Y |
| field sample result value is less than the minimum reporting level | N |
| field sample result value is more than the maximum reasonable value | Y |
| field sample result value is not null with indication of below minimum reporting level | N |
| field sample result value is null with no indication of below minimum reporting level | N |
| lab fortified sample matrix duplicate result value is less than 0.0001 | N |
| lab fortified sample matrix duplicate result value is less than one tenth of the minimum reporting level | Y |
| lab fortified sample matrix duplicate result value is more than the maximum reasonable value | Y |
| lab fortified sample matrix result value is less than 0.0001 | N |
| lab fortified sample matrix result value is less than one tenth of the minimum reporting level | Y |
| lab fortified sample matrix result value is more than the maximum reasonable value | Y |

UCMR XML

Click here to download the XML Schema.

Cory will provide the location!

## UCMR File Structure Tree Diagram

This section provides a graphical depiction of the UCMR file structure. It is not possible to provide a picture of the entire tree diagram at once due to size limitations. In order to present the tree diagram, we broke the file structure into four sections. Each section shows the detail for a specific portion of the file structure.

Reading from left to right and top to bottom, Figure 4 shows the root element of SafeDrinkingWaterSubmission and its sub-elements, TransactionPurposeIdentifier and SamplingEventDetails.  The sub-elements of SamplingEventDetails are also shown in Figure 4. The SchedulerIdentifierDetails section can be seen in Figure 5 and the SampleDetails section of the file structure can be seen in Figures 6.

Figure 4. SafeDrinkingWaterSubmission Tree Diagram – Root Element and sub-elements

Figure 5 shows the sub-element SamplingEventDetails and its sub-elements, SchedulerIdentifierDetails, SampleCollectionDate and SampleDetails.  The sub-elements of SchedulerIdentifierDetails are also shown in Figure 5.

Figure 5. SafeDrinkingWaterSubmission Tree Diagram with SchedulerIdentifierDetails

Figure 6 shows the sub-element SampleDetails and its sub-elements, SampleIdentifier, LaboratoryIdentificationCode, LaboratoryCommentText, and SampleMethodAnalyteDetails. The sub-elements of SampleMethodAnalyteDetails are also shown in Figure 6.

Figure 6. SafeDrinkingWaterSubmission Tree Diagram with SampleMethodAnalyteDetails

Logical Structure

This section contains tables defining the UCMR file content models. Each section is titled with the parent or container element and is followed by a table that lists the children or the contents of the container. The sub-element column indicates the sub-element name. The description column defines the element in the sub-element column of the table. A more detailed definition with element attributes and associated code lists (e.g., Analyte Code List and Method Code List) is in UCMR Data Dictionary section.

Namespace

All elements belong to the namespace:

http://www.exchangenetwork.net/schema/sdwars/1

The SafeDrinkingWaterSubmission Element

The root element for the UCMR XML document is SafeDrinkingWaterSubmission, as shown in Table 5. There are two elements below the root element. They are TransactionPurposeIdentifier and SamplingEventDetails. Table 6 describes the SamplingEventDetails sub-element.

Table 5. Top-Level Sub-Elements of SafeDrinkingWaterSubmission

| Sub-element | Description |
| --- | --- |
| TransactionPurposeIdentifier | This sub-element identifies the type of backend processing. |
| SamplingEventDetails | This sub-element contains the sample event related data elements. |

SamplingEventDetails Sub-Element

This container sub-element contains secondary sub-elements that hold the sample event related data elements. Table 7 describes the ScheduleIdentifierDetails sub-element and Table 8 describes the SampleDetails sub-element.

Table 6. SamplingEventDetails Sub-Elements

| Sub-element | Description |
| --- | --- |
| ScheduleIdentifierDetails | This sub-element contains schedule related data elements. |
| SampleCollectionDate | The date the sample is collected. |
| SampleDetails | This sub-element contains sample related data elements. |

ScheduleIdentifierDetails Sub-Element

This container sub-element contains secondary sub-elements that hold the schedule related data elements.

Table 7. ScheduleIdentifierDetails Sub-Elements

| Sub-element | Description |
| --- | --- |
| PublicWaterSystemCode | This sub-element is the code used to identify each PWS. |
| FacilityIdentifier | This sub-element is an identification code established by the state or, at the state’s discretion, by the PWS, following the format of a 5-digit number unique within each PWS for each applicable facility. |
| SamplePointIdentifier | This sub-element is an identification code established by the state, or at the state’s discretion, by the PWS, unique within each applicable facility, for each applicable sampling location. |
| ScheduleEventCode | This sub-element indicates the sequence number associated with the specific event. |
| MonitorTypeCode | This sub-element is the code identifying list 1 (AM) or list 2 (SS) monitoring. |

SampleDetails Sub-Element

This container sub-element contains secondary sub-elements that hold the sample related data elements. Table 9 describes the SampleMethodAnalyteDetails sub-element.

Table 8. SampleDetails Sub-Elements

| Sub-element | Description |
| --- | --- |
| SampleIdentifier | This sub-element uniquely identifies containers, or groups of containers, which hold the water samples collected at the same sampling location during the same sample collection date. |
| LaboratoryIdentificationCode | This sub-element is the code, assigned by EPA, used to identify each laboratory. |
| LaboratoryCommentText | This sub-element is used for ancillary information about the laboratory. |
| SampleMethodAnalyteDetails | This sub-element contains method analyte related data elements. |

SampleMethodAnalyteDetails Sub-Element

This container sub-element contains secondary sub-elements that hold the method analyte related data elements.

Table 9. SampleMethodAnalyteDetails Sub-Elements

| Sub-element | Description |
| --- | --- |
| MethodCode | This sub-element is the identification code of the analytical method used. |
| AnalyteCode | This sub-element is the identification code of the analyte being analyzed. |
| SampleTypeCode | This sub-element identifies the type of sample collected and/or prepared, as well as the fortification level. |
| ResultMeasure | This sub-element contains the actual numeric value of the analysis for chemical and microbiological results for: field samples; laboratory fortified matrix samples; laboratory fortified sample matrix duplicates; and concentration fortified. |
| ResultBelowMinimumReportingLevelIndicator | This sub-element is a "Yes/No" indicator specifying whether the ResultMeasure value was below the measurable threshold for this analyte. |
| ReviewStatusIdentifier | This sub-element is the identifier indicating the review status of this sample method analyte data set. |

UCMR Data Dictionary

Introduction

This section contains the data dictionary for the UCMR schema. This section also contains introductory materials about how to read the data dictionary. Only the data content elements are defined here. Group defining elements have a description in the logical structure of the UCMR File Structure Tree Diagram section.

How to Read This Data Dictionary

The data dictionary contains the element name, definition of the element, characteristics for the element, its relationship in the hierarchy, and a code list (when applicable). Below you will find further explanation for each segment of the definition in the dictionary structure.

Element Name

Definition:

This section provides a textual definition of the element and how it is used in the schema.

Characteristics:

The characteristics of an element provide information on the use of the element. Characteristics include data type (alpha- numeric or numeric), size or string length, requirement of optional or mandatory, and occurrences.

Parent Hierarchy:

The parent hierarchy section gives the relationship of the element to the root element.

Code List:

The code list presents all valid values for a particular “code” element, when applicable.

A Elements

AnalyteCode

Definition:

This element is the identification code of the analyte being analyzed. The analyte must be applicable for the Method provided.  See Appendix A – Analytes-to-Methods for a list of Methods and their Analytes.

Characteristics:

Data Type:	AlphaNumeric

Size:		1-4

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SampleMethodAnalyteDetails

Code List:

| Analyte Code | Analyte Name |
| --- | --- |
| 2004 | alachlor ESA |
| 2027 | acetochlor |
| 2045 | metolachlor |
| 2051 | alachlor |
| 2096 | hexahydro-1,3,5-trinitro-1,3,5-triazine |
| 2221 | dimethoate |
| 2314 | N-nitroso-dimethylamine |
| 2316 | N-nitroso-di-n-propylamine |
| U001 | terbufos sulfone |
| U002 | 2,2',4,4'-tetrabromodiphenyl ether |
| U003 | 2,2',4,4',5-pentabromodiphenyl ether |
| U004 | 2,2',4,4',5,5'-hexabromobiphenyl |
| U005 | 2,2',4,4',5,5'-hexabromodiphenyl ether |
| U006 | 2,2',4,4',6-pentabromodiphenyl ether |
| U007 | 1,3-dinitrobenzene |
| U008 | 2,4,6-trinitrotoluene |
| U009 | alachlor OA |
| U010 | acetochlor ESA |
| U011 | acetochlor OA |
| U012 | metolachlor ESA |
| U013 | metolachlor OA |
| U014 | N-nitroso-diethylamine |
| U015 | N-nitroso-di-n-butylamine |
| U016 | N-nitroso-methylethylamine |
| U017 | N-nitroso-pyrrolidine |

F Elements

FacilityIdentifier

Definition:

This element is an identification code established by the state or, at the state’s discretion, by the PWS, following the format of a 5-digit number unique within each PWS for each applicable facility. Leading zeros are required.

Characteristics:

Data Type:	N

Size:		5

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

ScheduleIdentifierDetails

L Elements

LaboratoryCommentText

Definition:

This element is used for ancillary information about the laboratory.

Characteristics:

Data Type:	AlphaNumeric

Size:		1-4000

Requirement:	Optional

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

LaboratoryIdentificationCode

Definition:

This element is the code, assigned by EPA, used to identify each laboratory. The code usually begins with the standard 2-character postal state abbreviation or region code and the remaining 5 numbers are unique to each Lab in the state.

Characteristics:

Data Type:	AlphaNumeric

Size:		7

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

M Elements

MethodCode

Definition:

This element is the identification code of the analytical method used. Labs must be approved for a method, as displayed on the Lab home page.

Characteristics:

Data Type:	AlphaNumeric

Size:		1-20

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SampleMethodAnalyteDetails

Code List:

| Method Code | Method Description |
| --- | --- |
| EPA 521 | EPA 521 |
| EPA 525.2 | EPA 525.2 |
| EPA 527 | EPA 527 |
| EPA 529 | EPA 529 |
| EPA 535 | EPA 535 |

MonitorTypeCode

Definition:

This element is the code identifying list 1 (AM) or list 2 (SS) monitoring.

Characteristics:

Data Type:	AlphaNumeric

Size:		2

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

ScheduleIdentifierDetails

Code List:

| Monitor Type Code | Monitor Type Description |
| --- | --- |
| AM | Assessment Monitoring (List 1) |
| SS | Screening Survey (List 2) |

P Elements

PublicWaterSystemCode

Definition:

This element is the code used to identify each PWS which usually begins with the standard 2-character postal state abbreviation or region code and the remaining 7 numbers are unique to each PWS in the state, with the exception of Utah where the code is 4 characters followed by 5 digits.

Characteristics:

Data Type:	AlphaNumeric

Size:		9

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

ScheduleIdentifierDetails

R Elements

ResultBelowMinimumReportingLevelIndicator

Definition:

This element is a "Yes/No" indicator specifying whether the ResultMeasure value was below the measurable threshold for this analyte. If ResultMeasure is provided, this must be “n” or non-existent.

Characteristics:

Data Type:	AlphaNumeric

Size:		1

Requirement:	Optional

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SampleMethodAnalyteDetails

Code List:

| Result Below MRL Code | Result Below MRL Description |
| --- | --- |
| N | No |
| Y | Yes |

ResultMeasure

Definition:

This element contains the actual numeric value of the analysis for chemical and microbiological results for: field samples; laboratory fortified matrix samples; laboratory fortified sample matrix duplicates; and concentration fortified. If a value is provided, ResultBelowMinimumReportingLevelIndicator must be “n” or non-existent.

Characteristics:

Data Type:	N

Size:		0.00000-99999.99999

Requirement:	Optional

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SampleMethodAnalyteDetails

ReviewStatusIdentifier

Definition:

This element the identifier indicating the review status of this sample method analyte data set.

Characteristics:

Data Type:	AlphaNumeric

Size:		2

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SampleMethodAnalyteDetails

Code List:

| Review Status Code | Review Status Description |
| --- | --- |
| 10 | Lab Hold |
| 30 | Lab Approve |

S Elements

SampleCollectionDate

Definition:

The date the sample is collected. This must not be a future date.

Characteristics:

Data Type:	Date

Size:		YYYYMMDD

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleIdentifier

Definition:

This element uniquely identifies containers, or groups of containers, which hold the water samples collected at the same sampling location during the same sample collection date. This value must be unique for the lab.

Characteristics:

Data Type:	AlphaNumeric

Size:		1-30

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SamplePointIdentifier

Definition:

This element is an identification code established by the state, or at the state’s discretion, by the PWS, unique within each applicable facility, for each applicable sampling location. This element must contain only letters and numbers (a-z, A-Z, 0-9).

Characteristics:

Data Type:	AlphaNumeric

Size:		1-20

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

ScheduleIdentifierDetails

SampleTypeCode

Definition:

This element identifies the type of sample collected and/or prepared, as well as the fortification level.

Characteristics:

Data Type:	AlphaNumeric

Size:		1-5

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

SampleDetails

SampleMethodAnalyteDetails

Code List:

| Sample Type Code | Sample Type Description |
| --- | --- |
| CF | Concentration Fortified |
| FS | Field Sample |
| LFSM | Lab Fortified Sample Matrix |
| LFSMD | Lab Fortified Sample Matrix Duplicate |

ScheduleEventCode

Definition:

This element indicates the sequence number associated with the specific event.

Characteristics:

Data Type:	AlphaNumeric

Size:		3

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

SamplingEventDetails

ScheduleIdentifierDetails

Code List:

| Schedule Event Code | Schedule Event Description |
| --- | --- |
| SE1 | Schedule Event 1 |
| SE2 | Schedule Event 2 |
| SE3 | Schedule Event 3 |
| SE4 | Schedule Event 4 |

T Elements

TransactionPurposeIdentifier

Definition:

The date the sample is collected.

Characteristics:

Data Type:	AlphaNumeric

Size:		1

Requirement:	Mandatory

Occurrences:	Once

Parent Hierarchy:

SafeDrinkingWaterSubmission

Code List:

| Transaction Purpose Identifier | Transaction Purpose Description |
| --- | --- |
| O | Original |
| R | Replacement |

Appendix A

Analytes-to-Methods

| Analyte Code | Method Code | Maximum Reasonable Value | Minimum Reporting Level |
| --- | --- | --- | --- |
| 2004 | EPA 535 | 300 | 1 |
| 2027 | EPA 525.2 | 99 | 2 |
| 2045 | EPA 525.2 | 99 | 1 |
| 2051 | EPA 525.2 | 99 | 2 |
| 2096 | EPA 529 | 99 | 1 |
| 2221 | EPA 527 | 70 | 0.7 |
| 2314 | EPA 521 | 0.99 | 0.002 |
| 2316 | EPA 521 | 0.99 | 0.007 |
| U001 | EPA 527 | 40 | 0.4 |
| U002 | EPA 527 | 30 | 0.3 |
| U003 | EPA 527 | 90 | 0.9 |
| U004 | EPA 527 | 70 | 0.7 |
| U005 | EPA 527 | 80 | 0.8 |
| U006 | EPA 527 | 50 | 0.5 |
| U007 | EPA 529 | 80 | 0.8 |
| U008 | EPA 529 | 80 | 0.8 |
| U009 | EPA 535 | 300 | 2 |
| U010 | EPA 535 | 300 | 1 |
| U011 | EPA 535 | 300 | 2 |
| U012 | EPA 535 | 300 | 1 |
| U013 | EPA 535 | 300 | 2 |
| U014 | EPA 521 | 0.99 | 0.005 |
| U015 | EPA 521 | 0.99 | 0.004 |
| U016 | EPA 521 | 0.99 | 0.003 |
| U017 | EPA 521 | 0.99 | 0.002 |