Specifications for Solicitation 1-155-RCB.1146

Refrigerant:  Virgin (unused) 1,1,1,2 Tetrafluorethane (R-134a) shall conform to all requirements of the ARI-700 standard for new refrigerants.  The supplier shall provide an ARI-700 Certificate of Analysis for the delivery prior to unloading.  The delivery shall be made by tank truck (approximately 30, 000 to 40,000 pounds) to NASA Langley Research Center, building 648, Hampton, VA.   The supplier shall provide all hoses, fittings, pumps, and other equipment to connect to the R-134a storage tank.  The vapor and liquid connections on the storage tank are quick disconnect “E” series coupling, female dry-disconnect coupler, Hydraulics Inc., Part #CP00110P1G1B.  In past deliveries of R-134a, it has been necessary to connect the delivery truck to both the liquid and the vapor side of the Langley storage tank in order to provide the pressure balance needed to pump the delivered liquid R-134a into the storage tank.  The Langley liquid storage tank, while primarily containing R-134a, may have a low mixture of air in the vapor layer that can contaminant the delivery truck.  Some recent vendors have overcome this problem by using an auxiliary pump on their tractor to pump the delivery trailer to a near vacuum (dumping the gas mixture back into the Langley storage tank).  Apparently the contamination level is considered acceptable at this reduced pressure condition.  The supplier shall provide a weight certificate at the time of delivery.