POLAR Spacecraft Status As of: Tues 22 July 03  12:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-11H Standby PM STIP data only | NOAA-12D Standby AM STIP data only | NOAA-14J Standby AM STIP data only | NOAA-15K BACKUP AM GAC data only | NOAA-16L PRIMARY PM GAC&LAC data | NOAA-17M PRIMARY AM GAC&LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 09/23/88 | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 |
| CNTL OBP | OBP2 | OBP2 | OBP2 OBP1 inoperative | OBP2 Non-encrypted command testing at Svaalbard 21-25 July | OBP2 | OBP2 |
| BUS | A-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS | DEGRADED (Y, Z- Gyros Failed) Reduced Gyro S/W | NOMINAL RGmode=Monitor | NOMINAL Rgmode=Disabled SS check Disabled when mode=YGC | OK Rgmode=Monitor Gyro-3 Off/Anom | NOMINAL Rgmode=Disabled Gyro IMU concerns Summit 24 July 1PM | NOMINAL Rgmode=Disabled |
| RXO | PRI BU random enables ETCUP +70 mSecs | PRI BU random enables | PRI BU random enables ETCUP –7.3 Msec | PRI ETCUP -8 mSec | PRI ETCUP –5.1 mSec | PRI ETCUP -1 msec |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | ON | ON | ON External Sync. Rephase Daily | ON External Sync, Rephase Daily. | ON External Sync, Rephase Enabled | ON Internal Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 1 | 2 Since 4/24/03 | 1 Analog telem drifting | 1 |
| DTRs | 1A, 2B, 3, 4A Safestate - 2B, | 1, 3, 4, 5B Safestate- 1B | 1, 2B, 3A, 5 Safestate- 1B | 1, 2, 3, 4 Safestate 1B EOT | 1,2,3,4A Safestate 3A 4B TOAR 418 (STIP only) | 1,2,3,4 Safestate=1B DTR2-SSR DTR5 TOAR 420 |
| VTX (APT data) | OFF | OFF since 7/12/03 Conflict with N15 back on 8/12/03 | OFF Since 8/14/02 (conflicts & poor AVHRR data) | 1 Conflict with N12 from 7/12 through 8/12 | INOP OFF since 11/15/00 | 2 |
| BTX | 2 | 1 | 2 | 1 | 1 | 2 |
| STX | 3 – TIP 1,2 - Playback | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 1, 2, 3 - degraded; 2 Omni–HRPT; 4- Playback | 1 – HRPT; 2– Playback; 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 1&2 Playback 4 – TIP |
| POWER (Array offset, charge and eclipse states, sun angle) | Array Off -30 Since 6/19/02 Eclipse all year Sun angle 78 Steady Trend Batts 1-3= LRC VT1,2=6/8 VT3 = 8/11 Charge state safe trip disabled | ArrayOff -45 since 7/10/03 considering move to –60 Eclipse Season Ends 8/25 Sun Angle at 36 trend down to 16 on 10/17 Batts 1&2=LRC V/T=4 | Array Off -45 Since 6/19/03 Eclipse Season Ends 8/15 Sun Angle at 33 trend down to 22 Batts 1-3= LRC Batt 1&3V/T=8/11 Batt2 VT=9/11 ) Shunt Degradation TOAR 425 | Array Off -45 Since 1/25/01 Eclipse Season Ends 8/4 Sun Angle at 31 trend down to 14 on 10/8 Batts 1-3= LRC V/T=7/9 | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 68 Steady trend Batt2A Temps TOAR 403 Batts 1-3= LRC V/T=4/8 | Array Off. –35 Since 7/1/02 Eclipse all year Sun Angle at 68 Steady Trend Batts 1-3= LRC V/T=4/8 Batt2A temp TOAR 416 |
| AVHRR | OFF Failed Power Supply | ON Nominal | ON Scan Motor degraded 5/1/03 (but improving) STATUS=RED | ON Rare Scan motor surges. Last Incident 7/4/03 | ON Nominal (3B) 3A-B switch once per week over north pole next 10 weeks. Last switch 21 July 23:46 | ON Nominal (3A&B) 3A-B switch enabled |
| AMSU-A1 |  |  |  | ON Ch14 inoperative Ch11 inoperative | ON TOAR 415 on primary PLLO chans 9-14 bias shift. TOAR 417 on Backup PLLO Status=Yellow | ON TOAR 413 Chan-3 popcorn noise TOAR 414 on PLLO chans 9-14 bias shift. TOAR 421 on Channel-7 elevated NEDT’s noise |
| AMSU-A2 |  |  |  | ON | ON Space Position-2 | ON |
| AMSU-B |  |  |  | ON Bias in All Channels. Motor current surges most recent 7/12/03 | ON Space Position-3 | ON |
| HIRS | OFF Filter Wheel Anomaly | INOP Filter Wheel turned OFF 10/17/02. Electronics On | ON Operational | ON Operational FW in Hi power, FW Heaters OFF Filter Motor current surges. Last incident 7/12 | ON Nominal | ON 1 Pixel cross track misalignment . |
| MSU | INOP OFF, Antenna Failed | INOP Scan Motor OFF since 3/12/03 Electronics ON. | ON Scan motor and antenna problems |  |  |  |
| SSU | ON |  | ON |  |  |  |
| DCS | ON | ON | ON | ON | ON Nominal | ON Nominal |
| SARR | ON Low signal |  | ON | ON-A All AGC Mode Intermittent failures for 243MHz A&B | ON-A All AGC Mode (B-side Receiver in FG mode) 243 MhZ INOPERATIVE. | ON-A Nominal All AGC Mode |
| SARP | ON Nominal |  | OFF Failed Power Supply | ON Nominal RCVR B/W = 2 | ON Nominal RCVR B/W = 2 | ON Nominal |
| SEM |  | ON Elec-CH-HVPS=4 Prot-CH-HVPS=0 | ON Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Telescopes inoperative | ON Nominal E-CDEM-HVPS=2 Since 1/14/03 P-CDEM-HVPS=0 | ON Nominal E-CDEM-HVPS=4 P-CDEM-HVPS=4 since 4/15/03 | ON Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 since 2/18/03 |
| SBUV | INOP Grating motor OFF since 5/29/03 Electronics and Heater remain ON |  | ON Occasional Reduced Grating Drive Motion Reduced operations profile started 6/5/03 |  | ON Backup Diffuser in use since 6/16/03. (Imagery has improved) Primary diffuser has antenna deploy anomaly, TOAR 426 AMSU EMI causing erratic Behavior from PMT cathod, in range 3 No corrective action possible | ON Nominal Anode Mode |
| SADPOS |  |  |  | N/A | ON ENABLED MFactor =50% | ON ENABLED |
|  | N11 | N12 | N14 | N15 | N16 | N17 |

COMMENTS/CHANGES:

NOAA-11	No changes since previous report.

NOAA-12.  	For the first time in almost 2 years, a data set of greater than 24 continuous hours was obtained for N12 thereby

allowing more in-depth analysis of that spacecraft.  In analyzing this data, EMOSS power engineer Andy Miller has noticed a significant number of small surges in bus voltage that is indicative of continued shunt stress which motivated the recent previous 2 array moves to –45 degree offset.  Therefore, Andy is proposing that an additional adjustment to –60 degree offset be considered sometime in the near future and is awaiting a approval by NOAA management before implementing this next move.  Whether approved or not, at the beginning of October the sun angle (relative to the array position) will begin to shade the sun sensor and the array will have to moved again to a position of –30 degree offset for the duration of that month.

NOAA-14:	N14’s power situation remained nominal throughout the past reporting period and the spacecraft continues to have a

good power balance since the solar array adjustments last month.

N14 AVHRR scan motor current continued to improve during the past week as it has for the past 7 weeks and is approaching what could be considered nominal values where imagery should be of sustained high quality.  (Illustration 1).  No AVHRR images were available at the time this report was generated and so none are included in this report.

NOAA-15:	Preparation for Svalbard unencrypted command tests using STX-4 were initiated from 18-20 July by powering up

STX-4 (illustration 2) and switching the N15 spacecraft into unencrypted mode (out of stored commands) for one orbit per day using stored commands.  On 21 July, during 2 overlapping Fairbanks/Svalbard visibilities starting at 20:00Z the actual tests with Svalbard began.  On the first pass, Fairbanks ran CP DECRYPTF per SCR 116 to configure spacecraft and PACS for clear mode then turned over command authority over to Svalbard.  Svalbard successfully achieved command carrier lock with acceptable AGC levels but the Last Command Time was reached before any NOOOPS were transmitted by them and the spacecraft faded in clear mode.  On the second pass at 21:35Z, the spacecraft rose in clear mode and, for the first time, Svalbard successfully unlinked a NOOOP command in the clear mode.  After Svalbard commanding was complete, command authority was given back to Fairbanks who to successfully commanded the spacecraft back to encrypted mode.  This operation will be repeated each day at approximately the same time until 25 July in order to support METOP operational preparations.  Angelique Riley is EMOSS POC for these operations.

The N15 AMSU-B motor current, AVHRR scan motor current and HIRS filter motor current were all nominal during

the past week with no new surges. (illustration 3).

NOAA-16: 	The macro developed by EMOSS engineer Jon Woodward to switch the AVHRR to Channel 3A over the northern

polar region was successfully trigger twice in the past week; first on 19 July from 17:52 to 18:04Z and again on 21 July from 22:30 to 22:46Z (illustration 4).  Additional triggerings of this macro (always via realtime command at dates and times specified by Dr Xianggian Wu.  The next triggering is expected to be on or about 30 July.

Yaw update values were generally nominal during the past week (illustration 5).  However, the trend of the gyros and

IMU towards less than perfectly nominal performance remains a cause for concern.  Therefore, a “summit meeting” has been called for 24 July at 13:00 eastern time in the LCR Team Room at Suitland to discuss the following issues:

1.  NOAA-16 IMU performance, and related issues, plans for  configuration changes

2.  Plans for RGYRO testing and requirements/preparations for conducting the test

3.  Other related concerns with this series IMU (NOAA-15, DMSP, etc.).

This meeting will be chaired by EMOSS engineer Jim Sheperd and is open (via teleconference) to any interested party.  who can dial in by calling 301-817-4220 (or just 2000 if located at Suitland), wait for a dial tone, followed by 2 short beeps then Enter 1016* and then enter 1234#   If connected, 2 beeps indicates you are on the meet-me net

NOAA-17:	RF testing continues at Svaalbard. These tests dump GAC data over the Svaalbard site once or twice a day using a

variable combination of S-band transmitters and frequencies (often STX-4).  These tests are being conducted to validate the Svaalbard ground station capabilities ability to support METOP and will continue out of the schedule until August 23rd.  STX-4 appears to be performing in a nominal manner (illustration 6).

NOAA-N 	Level 2 Data base validation (Phase One) has been completed by the EMOSS team and delivery to NASA for their

review is expected to be on time (25 July).  A schedule for TTS time during the month of August when NASA and EMOSS engineers can review the data base to a Level 3 (Phase One) is being generated and will be distributed within the next week.  Phase Two data base validation will require CWS and PACS upgrades to be complete before being implemented.  Azi Dianat has been the EMOSS POC for all data base development efforts.

EMOSS engineers and management attended a CWS implementation meeting with NOAA management to determine the best method for ensuring that NOAA-N launches using the CWS (vs 3100) system.  A plan for functional testing, parallel operations, operational training and CWS primary operations was worked out by this group but all such processes are predicated on the timely receipt of a baseline CWS by the EMOSS team.

EMOSS is planning on sending an engineer to support the MHS pre flight model hand over review in Sunnyvale CA between 28 and 30 July.  An EMOSSS  POC has yet to be designated but will be either Tina Baucom or Jim Walters.  .

Illustration 1: N14 AVHRR Scan Motor Health Analysis

Illustration 2:  N15 STX-4 analysis

### Illustration 3:  N15 Payload component analysis

Illustration 4:  N16 AVHRR channel selection

Illustration 5:  N16 Yaw Update values since previous report.

Illustration 6:  N17 STX-4 Power and Thermal Analysis

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING July 18, 2003

| DAY/DATE | NOAA-11 | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 07/11 | -1539 msec | -072 msec | -050 msec | +048 msec | -025 msec | -014 msec |
| SAT. 07/12 | -1469 msec | -078 msec | -050 msec | +048 msec | -026 msec | -010 msec |
| SUN. 07/13 | -1699 msec | -081 msec | -048 msec | +047 msec | -025 msec | -009 msec |
| MON. 07/14 | -1029 msec | -088 msec | -047 msec | +049 msec | -025 msec | -007 msec |
| TUE. 07/15 | -1159 msec | N/A | -045 msec | +049 msec | -026 msec | -006 msec |
| WED. 07/16 | -1089 msec | -100 msec | -045 msec | +050 msec | -021 msec | -007 msec |
| THU. 07/17 | -1219 msec | -109 msec | -045 msec | +050 msec | -026 msec | -007 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-12:  As of 09/03/02 the TIP clock is corrected daily by +70 msec to compensate for drift.

NOAA-14:  As of 04/23/03 the TIP clock is corrected daily by –-7.3 msec to compensate for drift.

NOAA-15:  As of 04/23/03 the TIP clock is corrected daily by –-8 msec to compensate for drift.

NOAA-16:  As of 04/23/03 the TIP clock is corrected daily by –5.1 msec to compensate for drift.

NOAA-17:  As of 04/23/03 the TIP clock is corrected daily by -1 msec to compensate for drift.

N12:  ADDED 1250 mSecs to spacecraft command clock on 6 June

N14:  SUBTRACTED 150 msec from spacecraft command on 10 June.

N15:  ADDED 100 msec to spacecraft command clock on 10 June.

N16:  SUBTRACTED 100 msec from spacecraft command clock on 10 June.

N17:  SUBTRACTED 100 msec from spacecraft command clock on 10 June.

N17 Weekly CPU Scrub Report

NOAA-17 Scrubber Hits by Geographic Occurrence since 27 Jul 02:

Chart POC Kim Kolb

Red/Circle = CPU#1  Black/X = CPU#2

### NOAA-17 Scrubber Hits from 14 Jul 2003 through 20 Jul 2003

PACS DATA AVAILABILITY (%)

July 11, 2003 through July 17, 2003

JDAY 192-198

|  |  |  | NOAA15 | NOAA14 | NOAA11 | NOAA16 | NOAA17 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Friday | 07/11 | 192 | 100.0 | 100.0 | 100.0 | 100.0 | 100.0 |
| Saturday | 07/12 | 193 | 100.0 | 100.0 | 99.9 (a) | 100.0 | 100.0 |
| Sunday | 07/13 | 194 | 100.0 | 100.0 | 80.6 (b) | 100.0 | 100.0 |
| Monday | 07/14 | 195 | 100.0 | 100.0 | 69.6 (c) | 100.0 | 100.0 |
| Tuesday | 07/15 | 196 | 100.0 | 100.0 | 44.9 (d) | 100.0 | 100.0 |
| Wednesday | 07/16 | 197 | 100.0 | 100.0 | 85.5 (e) | 100.0 | 100.0 |
| Thursday | 07/17 | 198 | 100.0 | 100.0 | 99.8 (f) | 100.0 | 100.0 |

EMOSS POC for this chart Angelique Riley

Comments:

- Rev 76311/W: S1A noisy; 99.6% recovered 10DL 15PE.

- Rev 76325/W: S2B noisy; 97.5% recovered 4DL 27PE.

- Rev 76336/F: S4A noisy; 93.8% recovered 10DL 42PE.

- Rev 76353/F: S3A noisy; 98.6% recovered 1PE.

- Rev 76371/F: S4A noisy; 95.6% recovered 6DL.

- Rev 76384/F: S2B noisy; 99.3% recovered 11PE.

*N-11 STIP records were late during these times.

DTR Inf. (*):

NOAA-11        	DTR 1B -Inoperative.

DTR 2A/B -Frequently noisy

DTR 4B -Frequently noisy

DTR 5A/B -Inoperative

NOAA-12	DTR 5A -Inoperative.

DTR 2B -Occasionally noisy and short

NOAA-14	DTR 4A/B -Inoperative.

DTR 3B -Unreliable playbacks, Removed from operations.

DTR 2A -Inoperative, DOY/200

NOAA-15	DTR 5A/B - Inoperative

NOAA-16            DTR 5A/B -Inoperative

DTR 3A -safe state change 1B

DTR 4B –Inoperative 1/12/03

NOAA-17	DTR 5A/B-Inoperative 2/16/03 Anomaly

Acronyms:

DL – Drop lock(s)	PE - Parity Error(s)			DQR - Data Quality Report

BE - Bit Error(s)	DAR - Data Accountability Report	MFR - Multi-Function Receiver