November 30, 2005

Technical Specification for

the Radio Frequency Quadrupole (RFQ)

Vane Modulation for the Proton Driver

Fermilab Specification:  5500-ES-371026

| Revision | ER/ECO | Date | Description | Originated By | Approved By |
| --- | --- | --- | --- | --- | --- |
| None | ER # 8220 | 21-Dec-05 | Original Issue | T. Page | G. Apollinari |

1.0  	GENERAL

This document describes the vane modulation for the Radio Frequency Quadrupole (RFQ) whose specifications are given in Fermilab Specification 5500-ES-371025.   The technical drawing that compliments this document is 5520-ME-440197.

# GOVERNING EQUATIONS

2.1 Input Radial Matcher

The distance r from the RFQ axis to the electrode in the input radial matcher is given by the expression:

where:

=	distance from the axis to the electrode at cross section with exact 			quadrupole symmetry = 0.34 cm

= cell length

= relative velocity of injected beam

= RF field wavelength

= number of cells = 6.

Figure 2.1.1 shows the input matcher electrode profile.  Figure 2.1.2 shows the EM Studio model on the input matcher.

Figure 2.1.1. Input matcher electrode profile.

Figure 2.1.2. EM Studio model of input matcher.

2.2 Main RFQ

The modulation of the electrodes in the main part of the RFQ is sinusoidal with a constant vane tip radius, = 0.255 cm.  The distance from the axis to the electrode surface along the i-th cell is given by the following expressions:

for vertical plane,

for horizontal plane,

where:

= distance along the vanes

=	the coordinate of the beginning of the i-th cell; the beginning of the cell 		is the point with exact quadrupole symmetry

=	distance from the axis to the electrode at cross section with exact 			quadrupole symmetry

= i-th cell length; for constant synchronous phase

= modulation factor =

= minimum aperture (radius)

= relative velocity of particle

= RF field wavelength.

The modulation factor, , and cell length, , for each cell has been calculated with DESRFQ code and are shown in Section 3, Table 3.1 of this document.

Figure 2.2.1 shows the EM Studio model of the vane modulation while Figure 2.2.2 shows the cross section of the vane tips.

Figure 2.2.1.  EM Studio model of the vane modulation in main RFQ.

Figure 2.2.2.  Vane tip cross section.

2.3 Output radial matcher

The distance r from the RFQ axis to the electrode in the output radial matcher is given by the expressions:

where:

= 2.2168 cm

D = 12.5664 cm

= 13.7779 cm; this is the length of the output matcher.

Figure 2.3.1 shows the output matcher electrode profile.  Figure 2.3.2 shows the EM Studio model on the output matcher.

Figure 2.3.1.  Output matcher electrode profile.

Figure 2.3.2.  EM Studio model of input matcher.

# DESIGN PARAMETERS

Table 3.1 lists the modulation factor, , and cell length, , for each cell by cell number.

Table 3.1 Values of modulation factor and cell length by cell number.

|  | Cell number | Modulation, | Cell length, [cm] |
| --- | --- | --- | --- |
| Input radial matcher | 1 |  | 2.8554 |
| Main RFQ | 2 | 1.025 | 0.4762 |
|  | 3 | 1.025 | 0.4762 |
|  | 4 | 1.025 | 0.4763 |
|  | 5 | 1.025 | 0.4763 |
|  | 6 | 1.025 | 0.4763 |
|  | 7 | 1.025 | 0.4763 |
|  | 8 | 1.025 | 0.4763 |
|  | 9 | 1.025 | 0.4763 |
|  | 10 | 1.025 | 0.4763 |
|  | 11 | 1.025 | 0.4763 |
|  | 12 | 1.025 | 0.4763 |
|  | 13 | 1.025 | 0.4764 |
|  | 14 | 1.025 | 0.4764 |
|  | 15 | 1.025 | 0.4764 |
|  | 16 | 1.025 | 0.4764 |
|  | 17 | 1.025 | 0.4764 |
|  | 18 | 1.028 | 0.4765 |
|  | 19 | 1.031 | 0.4765 |
|  | 20 | 1.034 | 0.4766 |
|  | 21 | 1.037 | 0.4766 |
|  | 22 | 1.04 | 0.4767 |
|  | 23 | 1.043 | 0.4768 |
|  | 24 | 1.046 | 0.4768 |
|  | 25 | 1.049 | 0.4769 |
|  | 26 | 1.052 | 0.4769 |
|  | 27 | 1.055 | 0.4770 |
|  | 28 | 1.058 | 0.4771 |
|  | 29 | 1.061 | 0.4772 |
|  | 30 | 1.064 | 0.4772 |
|  | 31 | 1.067 | 0.4773 |
|  | 32 | 1.07 | 0.4774 |
|  | 33 | 1.071 | 0.4774 |
|  | 34 | 1.072 | 0.4775 |
|  | 35 | 1.073 | 0.4775 |
|  | 36 | 1.074 | 0.4776 |
|  | 37 | 1.075 | 0.4776 |
|  | 38 | 1.076 | 0.4777 |
|  | 39 | 1.077 | 0.4777 |
|  | 40 | 1.078 | 0.4778 |
|  | 41 | 1.079 | 0.4782 |
|  | 42 | 1.08 | 0.4783 |
|  | 43 | 1.081 | 0.4784 |
|  | 44 | 1.082 | 0.4785 |
|  | 45 | 1.083 | 0.4786 |
|  | 46 | 1.084 | 0.4787 |
|  | 47 | 1.085 | 0.4789 |
|  | 48 | 1.086 | 0.4791 |
|  | 49 | 1.087 | 0.4793 |
|  | 50 | 1.088 | 0.4796 |
|  | 51 | 1.089 | 0.4798 |
|  | 52 | 1.09 | 0.4801 |
|  | 53 | 1.091 | 0.4804 |
|  | 54 | 1.092 | 0.4807 |
|  | 55 | 1.093 | 0.4811 |
|  | 56 | 1.094 | 0.4815 |
|  | 57 | 1.095 | 0.4819 |
|  | 58 | 1.095 | 0.4823 |
|  | 59 | 1.096 | 0.4828 |
|  | 60 | 1.096 | 0.4832 |
|  | 61 | 1.097 | 0.4837 |
|  | 62 | 1.097 | 0.4843 |
|  | 63 | 1.098 | 0.4848 |
|  | 64 | 1.098 | 0.4854 |
|  | 65 | 1.098 | 0.4860 |
|  | 66 | 1.098 | 0.4866 |
|  | 67 | 1.098 | 0.4873 |
|  | 68 | 1.098 | 0.4879 |
|  | 69 | 1.098 | 0.4886 |
|  | 70 | 1.099 | 0.4893 |
|  | 71 | 1.099 | 0.4901 |
|  | 72 | 1.099 | 0.4909 |
|  | 73 | 1.099 | 0.4917 |
|  | 74 | 1.099 | 0.4925 |
|  | 75 | 1.099 | 0.4933 |
|  | 76 | 1.0993 | 0.4942 |
|  | 77 | 1.0996 | 0.4951 |
|  | 78 | 1.0999 | 0.4960 |
|  | 79 | 1.1002 | 0.4970 |
|  | 80 | 1.1005 | 0.4980 |
|  | 81 | 1.1008 | 0.4990 |
|  | 82 | 1.1011 | 0.5000 |
|  | 83 | 1.1014 | 0.5011 |
|  | 84 | 1.1017 | 0.5022 |
|  | 85 | 1.102 | 0.5035 |
|  | 86 | 1.1023 | 0.5046 |
|  | 87 | 1.1026 | 0.5058 |
|  | 88 | 1.1029 | 0.5071 |
|  | 89 | 1.1032 | 0.5084 |
|  | 90 | 1.1035 | 0.5097 |
|  | 91 | 1.1038 | 0.5111 |
|  | 92 | 1.1041 | 0.5125 |
|  | 93 | 1.1044 | 0.5139 |
|  | 94 | 1.1047 | 0.5154 |
|  | 95 | 1.105 | 0.5169 |
|  | 96 | 1.1053 | 0.5185 |
|  | 97 | 1.1056 | 0.5201 |
|  | 98 | 1.1059 | 0.5218 |
|  | 99 | 1.1062 | 0.5235 |
|  | 100 | 1.1065 | 0.5252 |
|  | 101 | 1.1068 | 0.5270 |
|  | 102 | 1.1071 | 0.5289 |
|  | 103 | 1.1074 | 0.5307 |
|  | 104 | 1.1077 | 0.5327 |
|  | 105 | 1.108 | 0.5346 |
|  | 106 | 1.108217 | 0.5366 |
|  | 107 | 1.108434 | 0.5387 |
|  | 108 | 1.108651 | 0.5408 |
|  | 109 | 1.108868 | 0.5430 |
|  | 110 | 1.109085 | 0.5451 |
|  | 111 | 1.109302 | 0.5474 |
|  | 112 | 1.109519 | 0.5497 |
|  | 113 | 1.109736 | 0.5520 |
|  | 114 | 1.109953 | 0.5544 |
|  | 115 | 1.11017 | 0.5568 |
|  | 116 | 1.110387 | 0.5593 |
|  | 117 | 1.110604 | 0.5618 |
|  | 118 | 1.110821 | 0.5644 |
|  | 119 | 1.111038 | 0.5671 |
|  | 120 | 1.111255 | 0.5697 |
|  | 121 | 1.111472 | 0.5725 |
|  | 122 | 1.111689 | 0.5752 |
|  | 123 | 1.111906 | 0.5781 |
|  | 124 | 1.112123 | 0.5810 |
|  | 125 | 1.11234 | 0.5839 |
|  | 126 | 1.112557 | 0.5869 |
|  | 127 | 1.112774 | 0.5899 |
|  | 128 | 1.112991 | 0.5923 |
|  | 129 | 1.114233 | 0.5961 |
|  | 130 | 1.115466 | 0.5993 |
|  | 131 | 1.116699 | 0.6026 |
|  | 132 | 1.117932 | 0.6060 |
|  | 133 | 1.119165 | 0.6094 |
|  | 134 | 1.120398 | 0.6130 |
|  | 135 | 1.121631 | 0.6166 |
|  | 136 | 1.122864 | 0.6203 |
|  | 137 | 1.124097 | 0.6241 |
|  | 138 | 1.12533 | 0.6280 |
|  | 139 | 1.126563 | 0.6320 |
|  | 140 | 1.127796 | 0.6360 |
|  | 141 | 1.129029 | 0.6402 |
|  | 142 | 1.130262 | 0.6444 |
|  | 143 | 1.131495 | 0.6488 |
|  | 144 | 1.132728 | 0.6532 |
|  | 145 | 1.133961 | 0.6577 |
|  | 146 | 1.135194 | 0.6623 |
|  | 147 | 1.136427 | 0.6671 |
|  | 148 | 1.13766 | 0.6719 |
|  | 149 | 1.138893 | 0.6768 |
|  | 150 | 1.140126 | 0.6818 |
|  | 151 | 1.141359 | 0.6869 |
|  | 152 | 1.142592 | 0.6927 |
|  | 153 | 1.143825 | 0.6980 |
|  | 154 | 1.145058 | 0.7035 |
|  | 155 | 1.146291 | 0.7092 |
|  | 156 | 1.147524 | 0.7149 |
|  | 157 | 1.148757 | 0.7208 |
|  | 158 | 1.14999 | 0.7269 |
|  | 159 | 1.15299 | 0.7331 |
|  | 160 | 1.15599 | 0.7396 |
|  | 161 | 1.15899 | 0.7463 |
|  | 162 | 1.16199 | 0.7532 |
|  | 163 | 1.16499 | 0.7603 |
|  | 164 | 1.16799 | 0.7676 |
|  | 165 | 1.17099 | 0.7752 |
|  | 166 | 1.17399 | 0.7829 |
|  | 167 | 1.17699 | 0.7909 |
|  | 168 | 1.17999 | 0.7992 |
|  | 169 | 1.18529 | 0.8077 |
|  | 170 | 1.19059 | 0.8170 |
|  | 171 | 1.19589 | 0.8262 |
|  | 172 | 1.20119 | 0.8358 |
|  | 173 | 1.20649 | 0.8458 |
|  | 174 | 1.21179 | 0.8561 |
|  | 175 | 1.21709 | 0.8668 |
|  | 176 | 1.22239 | 0.8778 |
|  | 177 | 1.22769 | 0.8893 |
|  | 178 | 1.23299 | 0.9011 |
|  | 179 | 1.23829 | 0.9132 |
|  | 180 | 1.24359 | 0.9257 |
|  | 181 | 1.24889 | 0.9386 |
|  | 182 | 1.25419 | 0.9519 |
|  | 183 | 1.25949 | 0.9655 |
|  | 184 | 1.26479 | 0.9794 |
|  | 185 | 1.27009 | 0.9943 |
|  | 186 | 1.27539 | 1.0090 |
|  | 187 | 1.28069 | 1.0241 |
|  | 188 | 1.28599 | 1.0395 |
|  | 189 | 1.29599 | 1.0555 |
|  | 190 | 1.30599 | 1.0721 |
|  | 191 | 1.31599 | 1.0892 |
|  | 192 | 1.32599 | 1.1073 |
|  | 193 | 1.33599 | 1.1256 |
|  | 194 | 1.34599 | 1.1444 |
|  | 195 | 1.35599 | 1.1639 |
|  | 196 | 1.37099 | 1.1840 |
|  | 197 | 1.38599 | 1.2049 |
|  | 198 | 1.40099 | 1.2265 |
|  | 199 | 1.41599 | 1.2495 |
|  | 200 | 1.43099 | 1.2726 |
|  | 201 | 1.44599 | 1.2964 |
|  | 202 | 1.46799 | 1.3211 |
|  | 203 | 1.48999 | 1.3467 |
|  | 204 | 1.51199 | 1.3740 |
|  | 205 | 1.53399 | 1.4015 |
|  | 206 | 1.55599 | 1.4299 |
|  | 207 | 1.57799 | 1.4591 |
|  | 208 | 1.59999 | 1.4891 |
|  | 209 | 1.62999 | 1.5201 |
|  | 210 | 1.65999 | 1.5520 |
|  | 211 | 1.68999 | 1.5849 |
|  | 212 | 1.71999 | 1.6186 |
|  | 213 | 1.74999 | 1.6532 |
|  | 214 | 1.77999 | 1.6885 |
|  | 215 | 1.80999 | 1.7246 |
|  | 216 | 1.83999 | 1.7613 |
|  | 217 | 1.86999 | 1.7986 |
|  | 218 | 1.89999 | 1.8364 |
|  | 219 | 1.92999 | 1.8748 |
|  | 220 | 1.95999 | 1.9136 |
|  | 221 | 1.98999 | 1.9528 |
|  | 222 | 1.98 | 1.9919 |
|  | 223 | 1.98 | 2.0260 |
|  | 224 | 1.98 | 2.0595 |
|  | 225 | 1.98 | 2.0969 |
|  | 226 | 1.98 | 2.1337 |
|  | 227 | 1.98 | 2.1700 |
|  | 228 | 1.98 | 2.2057 |
|  | 229 | 1.98 | 2.2410 |
|  | 230 | 1.98 | 2.2758 |
|  | 231 | 1.98 | 2.3101 |
|  | 232 | 1.98 | 2.3440 |
|  | 233 | 1.98 | 2.3774 |
|  | 234 | 1.98 | 2.4105 |
|  | 235 | 1.98 | 2.4431 |
|  | 236 | 1.98 | 2.4753 |
|  | 237 | 1.98 | 2.5072 |
|  | 238 | 1.98 | 2.5387 |
|  | 239 | 1.98 | 2.5699 |
|  | 240 | 1.98 | 2.6007 |
|  | 241 | 1.98 | 2.6312 |
|  | 242 | 1.98 | 2.6613 |
|  | 243 | 1.98 | 2.6912 |
|  | 244 | 1.98 | 2.7208 |
|  | 245 | 1.98 | 2.7500 |
|  | 246 | 1.98 | 2.7790 |
|  | 247 | 1.98 | 2.8077 |
|  | 248 | 1.98 | 2.8362 |
|  | 249 | 1.98 | 2.8643 |
|  | 250 | 1.98 | 2.8923 |
|  | 251 | 1.98 | 2.9199 |
|  | 252 | 1.98 | 2.9474 |
|  | 253 | 1.98 | 2.9746 |
|  | 254 | 1.98 | 3.0015 |
|  | 255 | 1.98 | 3.0283 |
|  | 256 | 1.98 | 3.0548 |
|  | 257 | 1.98 | 3.0811 |
|  | 258 | 1.98 | 3.1072 |
|  | 259 | 1.98 | 3.1331 |
|  | 260 | 1.98 | 3.1588 |
|  | 261 | 1.98 | 3.1843 |
|  | 262 | 1.98 | 3.2096 |
|  | 263 | 1.98 | 3.2348 |
|  | 264 | 1.98 | 3.2597 |
|  | 265 | 1.98 | 3.2845 |
|  | 266 | 1.98 | 3.3091 |
|  | 267 | 1.98 | 3.3335 |
| Transition cell | 268 | 1 | 4.5867 |
| Output matcher | 269 | 1 | 13.7779 |
|  |  | Total electrode length | 302.7199 |

# VANE MODULATION DATA

Table 4.1 is a sample of the data points that define the vane modulation geometry.  This data will be provided to in a separate spreadsheet.

Table 4.1 Vane modulation data points.

| Cell # | Longitudinal coordinate [cm] | Distance from axis to vertical electrode [cm] | Distance from axis to horizontal electrode [cm] |
| --- | --- | --- | --- |
| End of cell 249 | 228.24026 | 0.34 | 0.34 |
| Cell 250 | 228.38487 | 0.35749 | 0.32251 |
|  | 228.52948 | 0.37455 | 0.30545 |
|  | 228.6741 | 0.39076 | 0.28924 |
|  | 228.81871 | 0.40572 | 0.27428 |
|  | 228.96332 | 0.41906 | 0.26094 |
|  | 229.10794 | 0.43046 | 0.24954 |
|  | 229.25255 | 0.43963 | 0.24037 |
|  | 229.39716 | 0.44634 | 0.23366 |
|  | 229.54178 | 0.45044 | 0.22956 |
|  | 229.68639 | 0.45181 | 0.22819 |
|  | 229.83101 | 0.45044 | 0.22956 |
|  | 229.97562 | 0.44634 | 0.23366 |
|  | 230.12023 | 0.43963 | 0.24037 |
|  | 230.26485 | 0.43046 | 0.24954 |
|  | 230.40946 | 0.41906 | 0.26094 |
|  | 230.55407 | 0.40572 | 0.27428 |
|  | 230.69869 | 0.39076 | 0.28924 |
|  | 230.8433 | 0.37455 | 0.30545 |
|  | 230.98791 | 0.35749 | 0.32251 |
|  | 231.13253 | 0.34 | 0.34 |
| Cell 251 | 231.27852 | 0.32251 | 0.35749 |
|  | 231.42452 | 0.30545 | 0.37455 |
|  | 231.57052 | 0.28924 | 0.39076 |
|  | 231.71652 | 0.27428 | 0.40572 |
|  | 231.86251 | 0.26094 | 0.41906 |
|  | 232.00851 | 0.24954 | 0.43046 |
|  | 232.15451 | 0.24037 | 0.43963 |
|  | 232.3005 | 0.23366 | 0.44634 |
|  | 232.4465 | 0.22956 | 0.45044 |
|  | 232.5925 | 0.22819 | 0.45181 |
|  | 232.7385 | 0.22956 | 0.45044 |
|  | 232.88449 | 0.23366 | 0.44634 |
|  | 233.03049 | 0.24037 | 0.43963 |
|  | 233.17649 | 0.24954 | 0.43046 |
|  | 233.32249 | 0.26094 | 0.41906 |
|  | 233.46848 | 0.27428 | 0.40572 |
|  | 233.61448 | 0.28924 | 0.39076 |
|  | 233.76048 | 0.30545 | 0.37455 |
|  | 233.90647 | 0.32251 | 0.35749 |
|  | 234.05247 | 0.34 | 0.34 |
| Cell 252 | 234.19984 | 0.35749 | 0.32251 |
|  | 234.34721 | 0.37455 | 0.30545 |
|  | 234.49458 | 0.39076 | 0.28924 |
|  | 234.64195 | 0.40572 | 0.27428 |
|  | 234.78932 | 0.41906 | 0.26094 |
|  | 234.93669 | 0.43046 | 0.24954 |
|  | 235.08405 | 0.43963 | 0.24037 |
|  | 235.23142 | 0.44634 | 0.23366 |
|  | 235.37879 | 0.45044 | 0.22956 |
|  | 235.52616 | 0.45181 | 0.22819 |
|  | 235.67353 | 0.45044 | 0.22956 |
|  | 235.8209 | 0.44634 | 0.23366 |
|  | 235.96827 | 0.43963 | 0.24037 |
|  | 236.11564 | 0.43046 | 0.24954 |
|  | 236.26301 | 0.41906 | 0.26094 |
|  | 236.41038 | 0.40572 | 0.27428 |
|  | 236.55774 | 0.39076 | 0.28924 |
|  | 236.70511 | 0.37455 | 0.30545 |
|  | 236.85248 | 0.35749 | 0.32251 |
|  | 236.99985 | 0.34 | 0.34 |

# Inspection Parameters

| Azimuthal Field Non-uniformity | +/- 1.0% (max) | Bead pull at factory |
| --- | --- | --- |
| Longitudinal Field Non-uniformity | +/- 1.0% (max) |  |
| Quality Factor | >80% of calculated Q | Factory Measurement |
| Mechanical Accuracy of Vanes | +/- 50 μm (max) | CMM data from machining |
| Vane Accuracy after assembly | +/- 30 μm (RMS) | Vendor Q/A procedures TBD |
| Minimum Separation Between Quadrupole & Dipole Modes | 4 MHz | Measured at factory |

# Text boxes

Distance, z [cm]

Radius, r [cm]

Radius, r [cm]

Distance, z [cm]

2Re