Memorandum

# U.S. Department
of Transportation

## Federal Aviation
Administration

| Subject: | INFORMATION: Final Policy Statement; Diesel Engine Installation; PS-ACE100-2002-004 | Date: | May 15, 2003 |
| --- | --- | --- | --- |
| From: | Manager, Small Airplane Directorate, ACE-100 | Reply to Attn. of: | Peter Rouse (816) 329-4135 |
| To: | SEE DISTRIBUTION |  |  |

### Summary

The purpose of this policy statement is to help identify appropriate certification requirements for installation of a diesel engine into a small airplane.  It includes guidance related to methods of compliance as well as potential equivalent level of safety findings (ELOS) and special conditions.

Installation of diesel engines into part 23 airplanes may include design features not envisioned when 14 CFR part 23 was created.  This policy highlights areas where special conditions may be appropriate for these installations.  However, appropriate special conditions for each installation must be determined on a case-by-case basis in accordance with 14 CFR part 21, §§ 21.16, 21.17 and 14 CFR part 11.

The installation of a diesel engine in a small certificated airplane design is not considered a design change so substantial that it would require a new airplane Type Certificate (TC) under 14 CFR part 21, § 21.19.  Therefore, it is considered appropriate to install a certificated diesel engine into a certificated airplane using the Supplemental Type Certificate (STC) or Amended Type Certificate (ATC) process.

All proposed diesel engine installations, whether supplemental, amended or new TC projects, will be considered significant as defined in Order 8100.5.  Given the significance of the change, early program coordination between the Standards Office and the Aircraft Certification Office (ACO) is necessary.  The ACO is expected to notify the Standards Office of such projects promptly and forward certification project notifications and associated certification plans as soon as practical after project application.  The ACO will identify the technological areas of concern identified in this policy statement as well as any additional concerns and develop a G-1 issue paper to establish the certification basis.

- Discussion of Significant Issues

#### General

Engines are being proposed to be certificated for installation in aircraft, especially small airplanes and airships, that operate on compression ignition power cycles rather than spark ignition power cycles.  Some aircraft diesel engines have been type certificated with others expected in the near future.  Diesel engines, however, have not been utilized in type certificated airplanes in the United States for over 70 years.  While some historical experience may be useful, there are many new and novel issues to be addressed as modern diesel engine technology is integrated into modern aircraft.

#### Nomenclature

In 14 CFR part 23, the utilization of fuel requirements is often used as a proxy for engine type (reciprocating versus turbine; AvGas versus Jet A, respectively).  The phrase “reciprocating engine” is often shorthand for “operates on AvGas” and the phrase “turbine engine” is often shorthand for “operates on kerosene-based fuels.”  To date, this approach has been sufficient.  However, an aircraft diesel engine is typically a reciprocating engine that would operate on jet fuel, and it was not envisioned by the 14 CFR part 23 rules.  While this policy has been developed to address most of the known technical issues where diesel engine and gasoline engine requirements must be differentiated, there may be other assumptions built into the regulations that will need to be evaluated to determine the appropriate technical requirements.

For the purposes of this policy statement, the term "conventional reciprocating engine" will be used to describe spark ignition, reciprocating engines that run on AvGas.  For the purposes of this policy statement, the term "aircraft diesel engine," or "ADE," will be used to describe compression ignition, reciprocating engines that run on kerosene-based fuels.

#### Installation Manual

Title 14 CFR part 33, § 33.5, requires, as part of the engine type certification effort, that an instruction manual for installation and operation of the engine be prepared and approved prior to issuance of the engine TC.  14 CFR part 23, § 23.901, requires that engine installations comply with these instructions.  The applicable regulations identified in this policy statement (including potential special conditions), combined with the engine installation instructions, should provide a comprehensive list of installation requirements for most diesel engine installations.  In addition, the methods of compliance and potential ELOS's described in this policy statement should assist applicants and ACO engineers when assessing methods to demonstrate compliance to applicable regulations.

#### Fuels

The FAA's current understanding is that Jet A is the leading candidate for use in aircraft diesel engines; however, this does not rule out other fuels such as           #2 Diesel or some other alternative fuel (bio-diesel).  The engine Type Certificate Data Sheet (TCDS) identifies the approved fuel(s) for use in an aircraft diesel engine.  Any fuels to be used in aircraft diesel engines will need a specification and Type Certificate Data Sheet (TCDS) approval.

The fuel and additives required for the aircraft diesel engine will be determined as part of the 14 CFR part 33 certification process and will be specified on the engine TCDS and in the engine installation data.  For a small airplane powered with a reciprocating engine that operates on kerosene-based fuels, such as an aircraft diesel engine, certain “turbine engine” fuel-related requirements should be met in lieu of the gasoline fuel related requirements.  Additives needed for turbine fuels that will also be required by an aircraft diesel engine (such as anti-icing and biocide additives) will be called out on the engine TCDS and in the fuel specification listed in the TCDS.

The appropriate fuels and additives, consistent with both the engine certification and airframe certification, must also be specified on the aircraft TCDS.  However, when approaching an aircraft diesel engine installation project, certain aspects of the diesel engine and its certificated fuel requirements should be kept in mind.  For instance, the cetane number is the primary parameter that defines diesel engine fuel that is similar to octane rating for conventional reciprocating engines.  Using the appropriate cetane rated fuel in a diesel engine is critical to developing the appropriate power.  Commercial turbine fuels will probably not be given a cetane rating; therefore, aircraft diesel engines will be approved and certificated to operate on a specific turbine fuel(s).  Any additional limiting parameters or specifications for the fuel will need to be defined on the engine TCDS, in lieu of specifying cetane requirements.

If automotive diesel fuel is to be approved, appropriate specifications will need to be identified.  Approval of fuels that do not have a specification (such as protein or plant-based (biodiesel) fuels) is anticipated; these will be handled on a case-by-case basis as approval is requested.  While the engine certification process addresses these concerns, it is best to be aware of the possible complications of specifying appropriate fuels for an aircraft diesel engine and the associated airframe compatibility issues.  Compatibility of the fuel system materials (elastomers, sealants, seals, liners, hoses, composite parts, etc.) with the approved fuels for an aircraft diesel engine has to be established.

#### Engine Controls

Many new technology aircraft diesel engines utilize a Full Authority Digital Engine Control (FADEC) or Electronic Engine Control (EEC).  Such systems are not unique to aircraft diesel engines and are increasingly common on conventional reciprocating engines.  Previous aircraft FADEC installations have required a special condition addressing § 23.1309 -- Equipment, Systems and Installation.  This special condition is available from the Small Airplane Directorate Standards Office.  In addition, an appropriate airplane level analysis must be performed to determine appropriate levels of High Intensity Radiated Fields (HIRF) compliance, and the HIRF special condition will most likely be applied.  The software certification level will need to be compliant with the appropriate RTCA DO178 level as described in AC 23.1309-1C.

This policy statement briefly touches on the subject of FADEC installation; however, it is not intended to cover all of the aspects of FADEC installation.  A future policy statement covering FADEC installation into 14 CFR part 23 aircraft is currently being written.

#### Vibration

Aircraft diesel engines may yield a greater level of vibration than current aircraft propulsion systems.  This issue is based upon feedback from industry during the development of aircraft diesel engines.   As part of the basic compliance efforts for an aircraft diesel engine airplane, the effects of vibration levels higher than those typical for conventional reciprocating engine powered airplanes must be considered.  In addition, the one cylinder inoperative condition will need to be evaluated.  The primary concern is that the vibratory loads imparted to the airframe by an aircraft diesel engine may be in excess of the experience of the general aviation fleet, thereby reducing the margin of design safety.  The goal of this policy statement is to ensure that the aircraft fleet will have an equivalent or better level of safety without unnecessary regulatory requirements.

#### Regulatory Review

The following table is taken from 14 CFR part 23 with an emphasis on the sections that require more consideration when incorporating a diesel engine for aircraft use.  The following is the criteria for a special condition as defined in § 21.16:

“If the Administrator finds that the airworthiness regulations of this subchapter do not contain adequate or appropriate safety standards for an aircraft, aircraft engine, or propeller because of a novel or unusual design feature of the aircraft, aircraft engine or propeller, he prescribes special conditions and amendments thereto for the product.  The special conditions are issued in accordance with Part 11 of this chapter and contain such safety standards for the aircraft, aircraft engine or propeller as the Administrator finds necessary to establish a level of safety equivalent to that established in the regulations.”

The policy statement makes several references to special conditions due to the new and novel features of aircraft diesel engines.  The existing regulations lack the adequate or appropriate safety standards equivalent to those currently utilized by aircraft propulsion systems.  There are 14 potential special conditions identified in the regulations matrix that starts on the next page.  The sections annotated with an asterisk (*) highlight requirements that may be applicable via special condition or may have additional requirements applied via special condition.  See the appropriate text paragraph describing the potential criteria for the special condition.

| PART 21 and 23 – AIRWORTHINESS STANDARDS: NORMAL, UTILITY, ACROBATIC, AND COMMUTER CATEGORY AIRPLANES: Affected Regulations |
| --- |
| Section | Title | Applicability | Anticipated Differences and Rationale |
| 21.19 | Issue of type certificate: Normal, utility, acrobatic, commuter, and transport category aircraft; manned free balloons; special classes of aircraft; aircraft engines; propellers | Yes | None |
| 21.21* | Certification Procedures For Products and Parts | Yes | See comments regarding unsafe conditions. Special Condition(s) may apply – See paragraph text. |
| 23.1 | Applicability. | Yes | None |
| 23.2 | Special retroactive requirements. | Yes | None |
| 23.3 | Airplane categories. | Yes | None |
| Subpart B – Flight |
| GENERAL |
| 23.21 | Proof of compliance. | Yes | None |
| 23.23 | Load distribution limits. | Yes | None |
| 23.25 | Weight limits. | Yes | None |
| 23.29 | Empty weight and corresponding center of gravity | Yes | None |
| 23.31 | Removable ballast. | Yes | None |
| 23.33 | Propeller speed and pitch limits | Yes | None |
| PERFORMANCE |
| 23.45 | General. | Yes | None |
| 23.49 | Stalling period. | Yes | None |
| 23.51 | Takeoff speeds. | Yes | None |
| 23.53 | Takeoff performance. | Yes | None |
| 23.55 | Accelerate-stop distance. | Yes | None |
| 23.57 | Takeoff path. | Yes | None |
| 23.59 | Takeoff distance and takeoff run | Yes | None |
| 23.61 | Takeoff flight path. | Yes | None |
| 23.63 | Climb: General. | Yes | None |
| 23.65 | Climb: All engines operating | Yes | None |
| 23.66 | Takeoff climb: One-engine | Yes | None |
| 23.67 | Climb: One engine inoperative | Yes | None |
| 23.69 | Enroute climb/descent. | Yes | None |
| 23.71 | Glide: Single-engine airplanes. | Yes | See comment concerning glide characteristics in Subpart B General discussion. |
| 23.73 | Reference landing approach speed | Yes | None |
| 23.75 | Landing distance. | Yes | None |
| 23.77 | Balked landing. | Yes | None |
| FLIGHT CHARACTERISTICS |
| 23.141 | General. |  |  |
| CONTROLLABILITY AND MANEUVERABILITY |
| 23.143 | General. | Yes | None |
| 23.145 | Longitudinal control. | Yes | None |
| 23.147 | Directional and lateral control | Yes | None |
| 23.149 | Minimum control speed. | Yes | None |
| 23.151 | Acrobatic maneuvers. | Yes | None |
| 23.153 | Control during landings. | Yes | None |
| 23.155 | Elevator control force in maneuvers | Yes | None |
| 23.157 | Rate of roll. | Yes | None |
| TRIM |
| 23.161 | Trim. | Yes | None |
| STABILITY |
| 23.171 | General. | Yes | None |
| 23.173 | Static longitudinal stability. | Yes | None |
| 23.175 | Demonstration of static longitudinal stability | Yes | None |
| 23.177 | Static directional and lateral stability | Yes | None |
| 23.181 | Dynamic stability. | Yes | None |
| STALLS |
| 23.201 | Wings level stall. | Yes | None |
| 23.203 | Turning flight and accelerated turning stalls | Yes | None |
| 23.207 | Stall warning. | Yes | None |
| SPINNING |
| 23.221 | Spinning. | Yes | None |
| GROUND AND WATER HANDLING Characteristics |
| 23.231 | Longitudinal stability and control | Yes | None |
| 23.233 | Directional stability and control | Yes | None |
| 23.235 | Operation on unpaved surfaces | Yes | None |
| 23.237 | Operation on water. | Yes | None |
| 23.239 | Spray characteristics. | Yes | None |
| MISCELLANEOUS FLIGHT REQUIREMENTS |
| 23.251 | Vibration and buffeting. | Yes | See comment concerning vibration characteristics |
| 23.253 | High speed characteristics. |  |  |
| Subpart C – Structure |
| GENERAL |
| 23.301 | Loads. | Yes | None |
| 23.302 | Canard or tandem wing configuration | Yes | None |
| 23.303 | Factor of safety. | Yes | None |
| 23.305 | Strength and deformation. | Yes | None |
| 23.307 | Proof of structure. | Yes | None |
| FLIGHT LOADS |
| 23.321 | General. | Yes | None |
| 23.331 | Symmetrical flight conditions. | Yes | None |
| 23.333 | Flight envelope. | Yes | None |
| 23.335 | Design airspeeds. | Yes | None |
| 23.337 | Limit maneuvering load factors | Yes | None |
| 23.341 | Gust loads factors. | Yes | None |
| 23.343 | Design fuel loads. | Yes | None |
| 23.345 | High lift devices. | Yes | None |
| 23.347 | Unsymmetrical flight conditions. | Yes | None |
| 23.349 | Rolling conditions. | Yes | None |
| 23.351 | Yawing conditions. | Yes | None |
| 23.361* | Engine torque. | Yes | See comment concerning engine torque characteristics. NOTE sudden stoppage cases should be considered. Special Condition(s) may apply – See paragraph text. |
| 23.363 | Side load on engine mount | Yes | None |
| 23.365 | Pressurized cabin loads. | Yes | None |
| 23.367 | Unsymmetrical loads due to engine failure | Yes | None |
| 23.369 | Rear lift truss. | Yes | None |
| 23.371 | Gyroscopic and aerodynamic loads | Yes | None |
| 23.373 | Speed control devices. | Yes | None |
| CONTROL SURFACE AND SYSTEM LOADS |
| 23.391 | Control surface loads. | Yes | None |
| 23.393 | Loads parallel to hinge line | Yes | None |
| 23.395 | Control system loads. | Yes | None |
| 23.397 | Limit control forces and torques | Yes | None |
| 23.399 | Dual control system. | Yes | None |
| 23.405 | Secondary control system. | Yes | None |
| 23.407 | Trim tab effects. | Yes | None |
| 23.409 | Tabs. | Yes | None |
| 23.415 | Ground gust conditions. | Yes | None |
| HORIZONTAL STABILIZING AND BALANCING SURFACES |
| 23.421 | Balancing loads. | Yes | None |
| 23.423 | Maneuvering loads. | Yes | None |
| 23.425 | Gust loads. | Yes | None |
| 23.427 | Unsymmetrical loads. | Yes | None |
| VERTICAL SURFACES |
| 23.441 | Maneuvering loads. | Yes | None |
| 23.443 | Gust loads. | Yes | None |
| 23.445 | Outboard fins or winglets | Yes | None |
| AILERONS AND SPECIAL DEVICES |
| 23.455 | Ailerons. | Yes | None |
| 23.459 | Special devices. |  |  |
| GROUND LOADS |
| 23.471 | General. | Yes | None |
| 23.473 | Ground load conditions and assumptions | Yes | None |
| 23.477 | Landing gear arrangement. | Yes | None |
| 23.479 | Level landing conditions. | Yes | None |
| 23.481 | Tail down landing conditions | Yes | None |
| 23.483 | One-wheel landing conditions. | Yes | None |
| 23.485 | Side load conditions. | Yes | None |
| 23.493 | Braked roll conditions. | Yes | None |
| 23.497 | Supplementary conditions for tail wheels | Yes | None |
| 23.499 | Supplementary conditions for nose wheels | Yes | None |
| 23.505 | Supplementary conditions for skiplanes | Yes | None |
| 23.507 | Jacking loads. | Yes | None |
| 23.509 | Towing loads. | Yes | None |
| 23.511 | Ground load; unsymmetrical loads on multiple-wheel units | Yes | None |
| WATER LOADS |
| 23.521 | Water load conditions. | Yes | None |
| 23.523 | Design weights and center of gravity | Yes | None |
| 23.525 | Application of loads. | Yes | None |
| 23.527 | Hull and main float load factors | Yes | None |
| 23.529 | Hull and main float landing conditions | Yes | None |
| 23.531 | Hull and main float takeoff condition | Yes | None |
| 23.533 | Hull and main float bottom pressures | Yes | None |
| 23.535 | Auxiliary float loads. | Yes | None |
| 23.537 | Seawing loads. | Yes | None |
| EMERGENCY LANDING CONDITIONS |
| 23.561 | General. | Yes | None |
| 23.562 | Emergency landing dynamic conditions | Yes | None |
| FATIGUE EVALUATION |
| 23.571 | Metallic pressurized cabin structures | Yes | None |
| 23.572 | Metallic wing, empennage, and associated structures | Yes | See comment concerning vibration characteristics |
| 23.573 | Damage tolerance and fatigue evaluation of structure | Yes | See comment concerning vibration characteristics |
| 23.574 | Metallic damage tolerance and fatigue evaluation of commuter category airplanes | Yes | See comment concerning vibration characteristics |
| 23.575 | Inspections and other procedures | Yes | None |
| Subpart D – Design and Construction |
| 23.601 | General. | Yes | None |
| 23.603 | Materials and workmanship. | Yes | None |
| 23.605 | Fabrication methods. | Yes | None |
| 23.607 | Fasteners. | Yes | None |
| 23.609 | Protection of structure. | Yes | None |
| 23.611 | Accessibility provisions. | Yes | None |
| 23.613 | Material strength properties and design values | Yes | See comment concerning vibration characteristics |
| 23.619 | Special factors. | Yes | None |
| 23.621 | Casting factors. | Yes | None |
| 23.623 | Bearing factors. | Yes | None |
| 23.625 | Fitting factors. | Yes | None |
| 23.627 | Fatigue strength. | Yes | See comment concerning vibration characteristics |
| 23.629* | Flutter. | Yes | See comment concerning vibration characteristics. Special Condition(s) may apply – See paragraph text. |
| WINGS |
| 23.641 | Proof of strength. | Yes | None |
| CONTROL SURFACES |
| 23.651 | Proof of strength. | Yes | None |
| 23.655 | Installation. | Yes | None |
| 23.657 | Hinges. | Yes | None |
| 23.659 | Mass balance. | Yes | None |
| CONTROL SYSTEMS |
| 23.671 | General. | Yes | None |
| 23.672 | Stability augmentation and automatic and power-operated systems | Yes | None |
| 23.673 | Primary flight controls. | Yes | None |
| 23.675 | Stops. | Yes | None |
| 23.677 | Trim systems. | Yes | None |
| 23.679 | Control system locks. | Yes | None |
| 23.681 | Limit load static tests | Yes | None |
| 23.683 | Operation tests. | Yes | None |
| 23.685 | Control system details. | Yes | None |
| 23.687 | Spring devices. | Yes | None |
| 23.689 | Cable systems. | Yes | None |
| 23.691 | Artificial stall barrier system | Yes | None |
| 23.693 | Joints. | Yes | None |
| 23.697 | Wing flap controls. | Yes | None |
| 23.699 | Wing flap position indicator | Yes | None |
| 23.701 | Flap interconnection. | Yes | None |
| 23.703 | Takeoff warning system. | Yes | None |
| LANDING GEAR |
| 23.721 | General. | Yes | None |
| 23.723 | Shock absorption tests. | Yes | None |
| 23.725 | Limit drop tests. | Yes | None |
| 23.726 | Ground load dynamic tests | Yes | None |
| 23.727 | Reserve energy absorption drop test | Yes | None |
| 23.729 | Landing gear extension and restraction system | Yes | None |
| 23.731 | Wheels. | Yes | None |
| 23.733 | Tires. | Yes | None |
| 23.735 | Brakes. | Yes | None |
| 23.737 | Skis. | Yes | None |
| 23.745 | Nose/tail wheel steering. | Yes | None |
| FLOATS AND HULLS |
| 23.751 | Main float buoyancy. | Yes | None |
| 23.753 | Main float design. | Yes | None |
| 23.755 | Hulls. | Yes | None |
| 23.757 | Auxiliary floats. | Yes | None |
| PERSONNEL AND CARGO ACCOMMODATIONS |
| 23.771 | Pilot compartment. | Yes | None |
| 23.773 | Pilot compartment view. | Yes | None |
| 23.775 | Windshields and windows. | Yes | None |
| 23.777 | Cockpit controls. | Yes | See comment concerning single control levers. |
| 23.779 | Motion and effect of cockpit controls | Yes | See comment concerning single control levers. |
| 23.781 | Cockpit control knob shape | Yes | See comment concerning single control levers. |
| 23.783 | Doors. | Yes | None |
| 23.785 | Seats, berths, litters, safety belts, and shoulder harnesses | Yes | None |
| 23.787 | Baggage and cargo compartments | Yes | None |
| 23.791 | Passenger information signs. | Yes | None |
| 23.803 | Emergency evacuation. | Yes | None |
| 23.805 | Flightcrew emergency exits. | Yes | None |
| 23.807 | Emergency exits. | Yes | None |
| 23.811 | Emergency exit marking. | Yes | None |
| 23.812 | Emergency lighting. | Yes | None |
| 23.813 | Emergency exit access. | Yes | None |
| 23.815 | Width of aisle. | Yes | None |
| 23.831 | Ventilation. | Yes | None |
| PRESSURIZATION |
| 23.841 | Pressurized cabins. | Yes | None |
| 23.843 | Pressurization tests. | Yes | None |
| FIRE PROTECTION |
| 23.851 | Fire extinguishers. | Yes | None |
| 23.853 | Passenger and crew compartment interiors | Yes | None |
| 23.855 | Cargo and baggage compartment fire protection | Yes | None |
| 23.859 | Combustion heater fire protection | Yes | None |
| 23.863 | Flammable fluid fire protection | Yes | None |
| 23.865 | Fire protection of flight controls, engine mounts, and other flight structure | Yes | None |
| ELECTRICAL BONDING AND LIGHTNING PROTECTION |
| 23.867 | Electrical bonding and protection against lightning and static electricity | Yes | None |
| MISCELLANEOUS |
| 23.871 | Leveling means. | Yes | None |
| Subpart E – Powerplant |
| GENERAL |
| 23.901* | Installation. | Yes | See comment concerning unique installation concerns: vibration, one cylinder inoperative, catastrophic failure. Special Condition(s) may apply – See paragraph text. |
| 23.903 | Engines. | Yes | See comment concerning unique installation concerns: starting and stopping, restarting envelope. |
| 23.904 | Automatic power reserve system | Yes | None |
| 23.905 | Propellers. | Yes | None |
| 23.907* | Propeller vibration. | Yes | See comment concerning unique installation concerns: vibration characteristics and effects on propellers. Special Condition(s) may apply – See paragraph text. |
| 23.909 | Turbocharger systems. | Yes | None |
| 23.925 | Propeller clearance. | Yes | None |
| 23.929 | Engine installation ice protection | Yes | None |
| 23.933 | Reversing systems. | Yes | None |
| 23.934 | Turbojet and turbofan engine thrust | Yes | None |
| 23.937 | Turbopropeller-drag limiting systems. | Yes | None |
| 23.939 | Powerplant operating characteristics. | Yes | None |
| 23.943 | Negative acceleration. | Yes | None |
| FUEL SYSTEM |
| 23.951* | General. | Yes | See comment concerning water absorbtion characteristics of fuel. Note: turbine engine requirements are sometimes more relevant to apply due to the nature of the ADE fuel. Special Condition(s) may apply – See paragraph text. |
| 23.953 | Fuel system independence. | Yes | None |
| 23.954 | Fuel system lightning protection | Yes | None |
| 23.955* | Fuel flow. | Yes | See comment concerning fuel temperature and fuel pump requirements. Note: turbine engine requirements are sometimes more relevant to apply due to the nature of the ADE fuel. Special Condition(s) may apply – See paragraph text. |
| 23.957 | Flow between interconnected tanks | Yes | None |
| 23.959 | Unusable fuel supply. | Yes | None |
| 23.961 | Fuel system hot weather operation | Yes | See comment concerning fuel temperature. |
| 23.963 | Fuel tanks: General. | Yes | None |
| 23.965 | Fuel tank tests. | Yes | None |
| 23.967 | Fuel tank installation. | Yes | None |
| 23.969 | Fuel tank expansion space | Yes | None |
| 23.971 | Fuel tank sump. | Yes | See comment fuel Sump. |
| 23.973* | Fuel tank filler connection | Yes | See comment concerning fuel filler and also placard as called out in 23.1557. Note: turbine engine requirements are sometimes more relevant to apply due to the nature of the ADE fuel. Special Condition(s) may apply – See paragraph text. |
| 23.975 | Fuel tank vents and carburetor vapor vents | Yes | None |
| 23.977* | Fuel tank outlet. | Yes | See comment concerning fuel filtration and possibility of injection blockage. Note: turbine engine requirements are sometimes more relevant to apply due to the nature of the ADE fuel. Special Condition(s) may apply – See paragraph text. |
| 23.979 | Pressure fueling systems. | Yes | None |
| FUEL SYSTEM COMPONENTS |
| 23.991 | Fuel pumps. | Yes | See comment concerning fuel delivery. Note: turbine engine requirements are sometimes more relevant to apply due to the nature of the ADE operation. |
| 23.993 | Fuel system lines and fittings | Yes | None |
| 23.994 | Fuel system components. | Yes | None |
| 23.995 | Fuel valves and controls | Yes | None |
| 23.997 | Fuel strainer or filter | Yes | See comment concerning fuel filtration and possibility of injection blockage. Note: turbine engine requirements are sometimes more relevant to apply due to the nature of the ADE fuel. |
| 23.999 | Fuel system drains. | Yes | None |
| 23.1001 | Fuel jettisoning system. | Yes | None |
| OIL SYSTEM |
| 23.1011 | General. | Yes | None |
| 23.1013 | Oil tanks. | Yes | None |
| 23.1015 | Oil tank tests. | Yes | None |
| 23.1017 | Oil lines and fittings | Yes | None |
| 23.1019 | Oil strainer or filter | Yes | None |
| 23.1021 | Oil system drains. | Yes | None |
| 23.1023 | Oil radiators. | Yes | None |
| 23.1027 | Propeller feathering system. | Yes | None |
| COOLING |
| 23.1041 | General. | Yes | None |
| 23.1043 | Cooling tests. | Yes | None |
| 23.1045 | Cooling test procedures for turbine engine powered airplanes | Yes | None |
| 23.1047 | Cooling test procedures for reciprocating engine powered airplanes | Yes | None |
| LIQUID COOLING |
| 23.1061 | Installation. | Yes | None |
| 23.1063 | Coolant tank tests. | Yes | None |
| INDUCTION SYSTEM |
| 23.1091 | Air induction system. | Yes | None |
| 23.1093 | Induction system icing protection | Yes | None |
| 23.1095 | Carburetor deicing fluid flow rate | Yes | None |
| 23.1097 | Carburetor deicing fluid system capacity | Yes | None |
| 23.1099 | Carburetor deicing fluid system detail design | Yes | None |
| 23.1101 | Induction air preheater design | Yes | None |
| 23.1103 | Induction system ducts. | Yes | None |
| 23.1105 | Induction system screens. | Yes | None |
| 23.1107 | Induction system filters. | Yes | None |
| 23.1109 | Turbocharger bleed air system | Yes | None |
| 23.1111 | Turbine engine bleed air system | Yes | None |
| EXHAUST SYSTEM |
| 23.1121 | General. | Yes | None |
| 23.1123 | Exhaust system. | Yes | None |
| 23.1125 | Exhaust heat exchangers. | Yes | None |
| POWERPLANT CONTROLS AND ACCESSORIES |
| 23.1141 | Powerplant controls: General. | Yes | None |
| 23.1142 | Auxiliary power unit controls | Yes | None |
| 23.1143 | Engine controls. | Yes | None |
| 23.1145* | Ignition switches. | Yes | See comment concerning usage of 'ignition switch' as a means of engine shutdown; it is realized that 'ignition switch' is a misnomer when concerned with ADE. Special Condition(s) may apply – See paragraph text. |
| 23.1147 | Mixture controls. | Yes | None |
| 23.1149 | Propeller speed and pitch controls | Yes | None |
| 23.1153 | Propeller feathering controls. | Yes | None |
| 23.1155 | Turbine engine reverse thrust and propeller pitch settings below the flight regime | Yes | None |
| 23.1157 | Carburetor air temperature controls | Yes | None |
| 23.1163 | Powerplant accessories. | Yes | None |
| 23.1165* | Engine ignition systems. | Yes | See comment concerning FADEC usage. Special Condition(s) may apply – See paragraph text. |
| POWERPLANT FIRE PROTECTION |
| 23.1181 | Designated fire zones; regions included | Yes | None |
| 23.1182 | Nacelle areas behind firewalls | Yes | None |
| 23.1183 | Lines, fittings, and components | Yes | None |
| 23.1189 | Shutoff means. | Yes | None |
| 23.1191 | Firewalls. | Yes | None |
| 23.1192 | Engine accessory compartment diaphragm | Yes | None |
| 23.1193 | Cowling and nacelle. | Yes | None |
| 23.1195 | Fire extinguishing systems materials. | Yes | None |
| 23.1197 | Fire extinguishing agents. | Yes | None |
| 23.1199 | Extinguishing agent containers. | Yes | None |
| 23.1201 | Fire extinguishing systems | Yes | None |
| 23.1203 | Fire detector system. | Yes | None |
| Subpart F -- Equipment |
| GENERAL |
| 23.1301 | Function and installation. | Yes | None |
| 23.1303 | Flight and navigation instruments | Yes | None |
| 23.1305* | Powerplant instruments. | Yes | See comment concerning unique instrumentation required for ADE operation. Special Condition(s) may apply – See paragraph text. |
| 23.1307 | Miscellaneous equipment. | Yes | None |
| 23.1309 | Equipment, systems, and installations. | Yes | None |
| INSTRUMENTS: INSTALLATION |
| 23.1311 | Electronic display instrument systems | Yes | None |
| 23.1321 | Arrangement and visibility. | Yes | None |
| 23.1322 | Warning, caution, and advisory lights | Yes | None |
| 23.1323 | Airspeed indicating system. | Yes | None |
| 23.1325 | Static pressure system. | Yes | None |
| 23.1326 | Pitot heat indication systems | Yes | None |
| 23.1327 | Magnetic direction indicator. | Yes | None |
| 23.1329 | Automatic pilot system. | Yes | None |
| 23.1331 | Instruments using a power source | Yes | None |
| 23.1335 | Flight director systems. | Yes | None |
| 23.1337 | Powerplant instruments installation. | Yes | None |
| ELECTRICAL SYSTEMS AND EQUIPMENT |
| 23.1351 | General. | Yes | None |
| 23.1353 | Storage battery design and installation | Yes | None |
| 23.1357 | Circuit protective devices. | Yes | None |
| 23.1359 | Electrical system fire protection | Yes | None |
| 23.1361 | Master switch arrangement. | Yes | None |
| 23.1365 | Electric cables and equipment | Yes | None |
| 23.1367 | Switches. | Yes | None |
| LIGHTS |
| 23.1381 | Instrument lights. | Yes | None |
| 23.1383 | Taxi and landing lights | Yes | None |
| 23.1385 | Position light system installation | Yes | None |
| 23.1387 | Position light system dihedral angles | Yes | None |
| 23.1389 | Position light distribution and intensities | Yes | None |
| 23.1391 | Minimum intensities in the horizontal plane of position lights | Yes | None |
| 23.1393 | Minimum intensities in any vertical plane of position lights | Yes | None |
| 23.1395 | Maximum intensities in overlapping beams of position lights | Yes | None |
| 23.1397 | Color specifications. | Yes | None |
| 23.1399 | Riding light. | Yes | None |
| 23.1401 | Anticollision light system. | Yes | None |
| SAFETY EQUIPMENT |
| 23.1411 | General. | Yes | None |
| 23.1415 | Ditching equipment. | Yes | None |
| 23.1416 | Pneumatic de-icer boot system | Yes | None |
| 23.1419 | Ice protection. | Yes | None |
| MISCELLANEOUS EQUIPMENT |
| 23.1431 | Electronic equipment. | Yes | None |
| 23.1435 | Hydraulic systems. | Yes | None |
| 23.1437 | Accessories for multi-engine airplanes | Yes | None |
| 23.1438 | Pressurization and pneumatic systems | Yes | None |
| 23.1441 | Oxygen equipment and supply | Yes | None |
| 23.1443 | Minimum mass flow of supplemental oxygen | Yes | None |
| 23.1445 | Oxygen distribution system. | Yes | None |
| 23.1447 | Equipment standards for oxygen dispensing units | Yes | None |
| 23.1449 | Means for determining use of oxygen | Yes | None |
| 23.1450 | Chemical oxygen generators. | Yes | None |
| 23.1451 | Fire protection for oxygen equipment | Yes | None |
| 23.1453 | Protection of oxygen equipment from rupture | Yes | None |
| 23.1457 | Cockpit voice recorders. | Yes | None |
| 23.1459 | Flight recorders. | Yes | None |
| 23.1461 | Equipment containing high energy rotors | Yes | None |
| Subpart G – Operating Limitations and Information |
| 23.1501 | General. | Yes | None |
| 23.1505 | Airspeed limitations. | Yes | None |
| 23.1507 | Operating maneuvering speed. | Yes | None |
| 23.1511 | Flap extended speed. | Yes | None |
| 23.1513 | Minimum control speed. | Yes | None |
| 23.1519 | Weight and center of gravity | Yes | None |
| 23.1521* | Powerplant limitations. | Yes | See comment concerning unique operational requirements for ADE. Special Condition(s) may apply – See paragraph text. |
| 23.1522 | Auxiliary power unit limitations | Yes | None |
| 23.1523 | Minimum flight crew. | Yes | None |
| 23.1524 | Maximum passenger seating configuration | Yes | None |
| 23.1525 | Kinds of operation. | Yes | None |
| 23.1527 | Maximum operating altitude. | Yes | None |
| 23.1529 | Instructions for Continued airworthiness | Yes | None |
| MARKINGS AND PLACARDS |
| 23.1541 | General. | Yes | None |
| 23.1543 | Instrument markings: General. | Yes | None |
| 23.1545 | Airspeed indicator. | Yes | None |
| 23.1547 | Magnetic direction indicator. | Yes | None |
| 23.1549 | Powerplant and auxiliary power unit instruments | Yes | None |
| 23.1551 | Oil quantity indicator. | Yes | None |
| 23.1553 | Fuel quantity indicator. | Yes | None |
| 23.1555 | Control markings. | Yes | None |
| 23.1557* | Miscellaneous markings and placards | Yes | See comment concerning fuel placard for ADE. Special Condition(s) may apply – See paragraph text. |
| 23.1559 | Operating limitations placard. | Yes | None |
| 23.1561 | Safety equipment. | Yes | None |
| 23.1563 | Airspeed placards. | Yes | None |
| 23.1567 | Flight maneuver placard. | Yes | None |
| AIRPLANE FLIGHT MANUAL AND APPROVED MANUAL MATERIAL |
| 23.1581 | General. | Yes | None |
| 23.1583 | Operating limitations. | Yes | See comment concerning unique operational requirements for ADE. |
| 23.1585 | Operating procedures. | Yes | See comment concerning unique operational requirements for ADE. |
| 23.1587 | Performance information. | Yes | None |
| 23.1589 | Loading information. | Yes | None |

- Section Discussions

Part 21

## Primary Category

An aircraft diesel engine design cannot be approved as part of an airframe TC under a primary category approval.  The intent of primary category is a simple aircraft, and the aircraft diesel engine does not have any service history to warrant approval in the primary category without prior engine certification.  It would be allowable, per part 33, to put a certified diesel engine in a primary category airplane.  This position may change once the service history of the aircraft diesel engine is established.

#### Airships

The technical concerns mentioned in this policy should also be considered with respect to airship projects.

Legacy Aircraft Diesel Engines

There are three certificated diesel airplane engines from the 1930's and 1940's that the FAA is aware of:

Packard DR-980	ATC 43	1930

Guiberson A-980	ATC 79

Guiberson A-1020 	TC    220

(ATC -- Approved Type Certificate, TC -- Type Certificate).

The Packard went into limited trial service, and there is no knowledge if either of the Guiberson engines went into aircraft service.  In the unlikely event that one of these engines is proposed for installation, existing changed product policy should be applied, depending on the vintage of the airframe to be used.  The reliability of the Packard is considered substandard to conventional reciprocating engines of the same period, and if any of the Packard engines is to be installed in an airplane for other than experimental purposes, this must be considered.  It is extremely unlikely that any of the remaining Guiberson engines could be brought into suitable condition for installation in an aircraft, but similar considerations would apply.

Some of the original known airplane Packard diesel engine installation combinations include the following (some of these may not have been approved for standard operations):  Army (Consolidated) primary trainer, Bellanca "six place," Bellanca Special, Buhl Air Sedan, Ford Tri-Motor, Ryan "four place," Stewart Twin, Stinson Detroiter, Stinson Junior, Towle Amphibian, Verville Air Coach, and Waco Straight Wing.

§ 21.19 -- Changes Requiring a New Type Certificate

You may install a certificated aircraft diesel engine into a certificated airplane using either the STC or ATC process.  You may not install a certificated diesel engine into a certificated airplane through a field approval.  The design requirements appropriate to the aircraft diesel engine and its systems along with historical precedents justify this rationale.

§ 21.21(b)(2) Issue of Type Certificate; Normal, Utility, Acrobatic, Commuter, and Transport Category Aircraft; Manned Free Balloons; Special Classes of Aircraft; Aircraft Engines; Propellers (Special Condition -- Engine Vibration)

§ 21.21(b) states:

The applicant submits the type design, test reports, and computations necessary to show that the product to be certificated meets the applicable airworthiness, aircraft noise, fuel venting, and exhaust emission requirements of the Federal Aviation Regulations and any special conditions prescribed by the Administrator, and the Administrator finds─

§ 21.21(b)(2) states:

For an aircraft, that no feature or characteristic makes it unsafe for the category in which certification is requested.

Given the lack of field service history on aircraft diesel engines, the following special conditions will most likely be required for diesel engine installations:

(1) No unsafe condition will exist in case of an inoperable cylinder until the engine can be shut down and the resistance of the propeller, engine mount, and airframe structure to shaking moment/vibration damage is investigated.  It must be shown that the shaking and vibration damage from the engine (caused by an inoperative cylinder) will not cause a catastrophic airframe failure and no unsafe condition will exist.

(2) The propeller utilized on the engine must be certificated to survive such an event without catastrophic failure.  The concern is a catastrophic failure of the propeller in case of an inoperable cylinder.

Part 23

Subpart B – Flight

General Comment:  As with all air breathing engines, a diesel engine will lose performance at lower intake air densities.  The rate of change will be different for a diesel than either a conventional reciprocating engine (including turbocharged or supercharged) or a turbine engine.  The airplane performance effects need to be understood and documented in the airplane flight manual.  Airplane engine conversions should be evaluated thoroughly because a diesel engine's standard day rating may not be directly comparable to a conventional reciprocating engine.  In addition, the power-off glide characteristics with an aircraft diesel engine may be substantially different due to the effect of a wind milling or stopped propeller.

§ 23.251 -- Vibration and Buffeting

As part of the basic compliance efforts for aircraft diesel-powered engine airplanes, the effects of vibration levels higher than those typical for conventional reciprocating engine powered airplanes must be considered.  The concern is for engine excitation of the airframe within the certification flight envelope, especially at the limits of the flight envelope.

Subpart C -- Structure

§ 23.361 paragraphs (b)(1) and (c)(3) -- Engine Torque

The sudden stoppage criterion used for turbine engines is considered appropriate for aircraft diesel engines.  The sudden stoppage criterion is considered appropriate due to the much greater cylinder pressures and the potentially more severe failure mode of an aircraft diesel engine.  This may be applicable via a special condition.  The applicant can develop, in lieu of this, data that would show that an ELOS would be demonstrated with similar installations.

The factor of four, for aircraft diesel engines with four cylinders or more, will be used to multiply the aircraft diesel engine's mean torque to calculate the limit torque; this is due to the higher expected load levels in the diesel engines.  In the case of an aircraft diesel engine with less than four cylinders, the FAA will consider this on a case-by-case basis.  This may be applicable via a special condition.  The applicant can develop, in lieu of this, data that would show that an ELOS would be demonstrated with similar installations.

§ 23.572 -- Metallic Wing, Empennage, and Associated Structure

As part of the basic compliance efforts for aircraft diesel engine powered airplanes, the effects of vibration levels higher than those typical for conventional reciprocating engine powered airplanes must be considered.  There are no additional tests other than the basic compliance requirements.  The vibration surveys would be conducted at various points throughout the flight envelope and the data would be analyzed against the structure fatigue characteristics.  The concern is for any adverse effects on fatigue characteristics of the airframe.

The added weight due to the increased density of diesel fuel compared to AvGas will need to be evaluated when an aircraft diesel engine is being installed via STC into an already certificated aircraft.  AC 23-7 provides the appropriate guidance.

§ 23.573 -- Damage Tolerance and Fatigue Evaluation Structure

As part of the basic compliance efforts for aircraft diesel engine powered airplanes, the effects of vibration levels higher than those typical for conventional reciprocating engine powered airplanes must be considered.  Our concern is for any adverse effects on fatigue characteristics of the airframe.

§ 23.574 – Metallic Damage Tolerance and Fatigue Evaluation Structure of Commuter Category Airplanes

As part of the basic compliance efforts for aircraft diesel engine powered airplanes, the effects of vibration levels higher than those typical for conventional reciprocating engine powered airplanes must be considered.  Our concern is for any adverse effects on fatigue characteristics of the airframe.

Subpart D -- Design and Construction

§ 23.613 -- Material Strength Properties and Design Values

As part of the basic compliance efforts for aircraft diesel engine-powered airplanes, the effects of vibration levels higher than those typical for conventional reciprocating engine powered airplanes must be considered.  Our concern is any adverse effects on fatigue characteristics of the airframe.

§ 23.627 -- Fatigue Strength

As part of the basic compliance efforts for an aircraft diesel engine airplane, the effects of higher vibration levels that might be higher than those typical for conventional reciprocating engine powered airplanes must be considered.  Our concern is for any adverse effects on fatigue characteristics of the airframe.

§ 23.629, paragraphs (e)(1) and (2) -- Flutter

The vibration levels of the aircraft diesel engine will most likely require the application of the turbopropeller requirements by a special condition.  Considerations for vibration levels, including those with an inoperative cylinder, will need to be evaluated.  Our concern is for engine excitation of the airframe within the certification flight envelope.

When installing an aircraft diesel engine in an airplane, the applicant will show by test or analysis, or by a combination of methods, that, in the event of an inoperative cylinder, the airframe can withstand the shaking or vibratory forces imposed by the engine.  Diesel engines of conventional design typically have extremely high levels of vibration in the case of an inoperative cylinder.  The engine manufacturer should provide data to the airframe installer/modifier so that either of those appropriate design considerations or operating procedures, or both, can be developed to prevent airframe damage.

Under § 21.21(b)(2), the following requirement appears:  No feature or characteristic makes the aircraft unsafe for the category in which certification is requested.  This is of particular concern during an airplane engine conversion as the original design data is often not available and the engine/propeller is apt to be heavier as well as being subjected to higher vibratory loads.  As described earlier in this policy statement, there is a potential special condition applied to § 21.21(b)(2) concerning the one cylinder inoperative scenario and its potential to be an unsafe condition.

§ 23.629(i) -- Flutter

Considerations for vibration levels, including those with an inoperative cylinder, will need to be evaluated.  Our concern is for engine excitation of the airframe within the certification flight envelope.

Care must be taken for older aircraft, which will be changed and which have been certificated against a lower level of airworthiness requirements.  Principal ground vibration tests will most likely be necessary to show compliance with § 23.629 in terms of symmetric/asymmetric coupling between engine mass and empennage, especially elevator and horizontal stabilizer structure.

§ 23.777(d) -- Cockpit Controls

If a single power lever/single power control is used, the applicant will need to request an ELOS per AC 23-17A guidance.

§ 23.779(b) -- Motion and Effect of Cockpit Controls

If a single power lever/single power control is used, the applicant will need to request an ELOS per AC 23-17A guidance.

§ 23.781 -- Cockpit Control Knob Shape

If a single power lever/single power control is used, the applicant will need to request an ELOS per AC 23-17A guidance.

Subpart E -- Powerplant

§ 23.901 -- Installation

Based on limited historical precedent, but also on the fact that much higher cylinder pressures exist in diesel engines, the possibility that engine failures may lead to liberation of high energy engine fragments must be evaluated.  The applicant will submit a safety analysis that addresses the engine construction and possible failure modes.

The engine manufacturer should perform the safety analysis and supply the safety analysis as part of the engine design data.  If the safety analysis indicates that there may be an engine failure mode that will liberate engine parts, then the design features of the airplane must be configured to minimize the hazard to crew, controls, and passengers.  If the engine has failure modes that will liberate parts, then consequences of the failure must be analyzed and minimized; i.e., the probability of the failure will be 100 percent.  Mitigation of the failure hazard must include reasonable design features to achieve minimization and not merely be an analysis of the final design.  This requirement may be applied with a special condition.

§ 23.901(d)(1) -- Installation

The vibration levels of the aircraft diesel engine, if greater than those for conventional reciprocating engines, may require the application of this turbine engine requirement by a special condition.  Considerations for vibration levels, including those with an inoperative cylinder, will need to be evaluated.

When installing an aircraft diesel engine in an airplane, the applicant will show by test or analysis, or by a combination of methods, that in the event of an inoperative cylinder the engine and airframe can withstand the shaking or vibratory forces imposed by the engine.  Diesel engines of conventional design typically have extremely high levels of vibration in the case of an inoperative cylinder.  The engine manufacturer should provide data to the airframe installer/modifier so that either of those appropriate design considerations or operating procedures, or both, can be developed to prevent airframe damage.

Under § 21.21(b)(2), the following requirement appears:  No feature or characteristic makes the aircraft unsafe for the category in which certification is requested.  This is of particular concern during an airplane engine conversion as the original design data is often not available and the engine/propeller is apt to be heavier as well as being subjected to higher vibratory loads.  As described earlier in this policy statement, there is a potential special condition applied to § 21.21(b)(2) concerning the one cylinder inoperative scenario and its potential to be an unsafe condition.

There is no existing requirement for conventional reciprocating engines to ensure that the installed engine does not exceed the engine's vibratory limit under all operating conditions.  This requirement is in § 23.901(d)(1) and is applicable to turbine engines only.  A special condition may be needed to impose this requirement on any airplanes that use an aircraft diesel engine.

§ 23.903(f) -- Engines

Diesel engine starting systems may utilize unconventional starting technology.  Due to high compression levels of the diesel engine (or possibly environmental conditions), air starters or other systems may be used that may be expended or that have recharge times.  Also, high-pressure fuel systems are more susceptible to air lock conditions during altitude restart situations.  Limitations may have to be added that address these design features.  This would be considered a basic compliance issue.

§ 23.907 -- Propeller Vibration

The power cycle of the diesel engine is fundamentally different from a conventional reciprocating engine and may impose unacceptable loads, vibration levels, and vibration modes on propellers that have previously been approved and considered acceptable for gasoline or turbine engine installations.  Propeller vibration requirements must be substantiated by testing, as conventional propellers might not be robust enough to use on a diesel engine.

Aircraft diesel engine crankshafts typically have high first order torsionals, the propeller is likely to be quite rugged and possibly contain new and unusual design characteristics.  For the initial installations, the listing of propeller combinations approved vibration wise in a propeller TCDS, Note 9, would not be considered to be a showing of compliance to § 23.907.  The applicant must perform a vibration test and analysis to determine engine/propeller/airframe compatibility prior to the approval of the (certificated) engine and propeller installation in a certificated airplane.

§ 23.907(a)	Fixed pitch wooden propellers may not be excluded from

the requirement.  The requirement may be applied via

special condition.

§ 23.907(a)(1)		Required.

§ 23.907(a)(2)		Not acceptable for diesel engine installations at this time.

§ 23.907(a)(3)		Service history may not be acceptable for new technology.

§ 23.907(b)		Fixed pitch wooden propellers will not be excluded.  The

requirement will be applied via special condition.

§ 23.951(c) -- Fuel System -- General

The airplane will comply with the requirements of part 23, § 23.951(c), as kerosene-based fuels absorb greater amounts of water than gasoline fuels and have a much greater potential for fuel system icing.

Some turbine engine powered airplanes have complied with this requirement by mandating the utilization of fuel anti-icing additives.  Mandating the use of anti-icing additives would be an acceptable method to show compliance; however, the use of these additives is generally being curtailed in some countries for environmental reasons.  A special condition will likely be required to impose the requirements of § 23.951(c) on any airplanes that use an aircraft diesel engine and operate on kerosene-based fuels.

§ 23.955(a) -- Fuel Flow -- General

See the discussion concerning fuel temperature under § 23.961, § 23.1521(e) and fuel temperature limitations.

§ 23.955, paragraphs (c) and (f) -- Fuel Flow  -- Pump Systems

The minimum flow requirements of § 23.955(c) apply to pump systems for conventional reciprocating engines.  The requirement was developed to prevent detonation by ensuring that a rich mixture could always be attained.  The turbine engine requirements of § 23.955(f) are more suitable to an aircraft diesel engine because a diesel engine, which already operates lean of stoichiometric, does not have the same need to ensure a rich operating condition to prevent engine damage.  The certificated engine will address the issue of “detonation margin” and, if required, the 100 percent requirement of § 23.955(f) will be adjusted accordingly.  The requirement will be applied by a special condition if applicable to the installation.

§ 23.961 -- Fuel System Hot Weather Operation

The engine fuel injection system will most likely provide a high volume of return fuel.  This may lead to an excessive temperature rise of the fuel.  The acceptable fuel temperature limitation required by shall not be exceeded.  A test has to be performed to determine the fuel temperature under the worst condition.  The hot fuel test has to be performed under these conditions.

§ 23.971(c) -- Fuel Tank Sump

The purpose of the sediment bowl of the configuration specified in § 23.971(c) is to remove any water that separates from the gasoline.  Water is more soluble in kerosene fuels than in gasoline and a fuel sediment bowl may not be necessary based upon the experience of turbine powered airplanes.  This section might be deemed “not applicable” for an aircraft diesel engine.

§ 23.973(f) -- Fuel Tank Filler Connection

The fuel filler nozzle for turbine engine fuel (Jet-A) is larger than the corresponding fuel filler nozzle for conventional reciprocating engine fuel (100LL).  In order to minimize the potential for mis-fueling, the airplane should comply with the requirements of § 23.973(f) in lieu of § 23.973(e).  Also, see the § 23.1557 discussion in this policy statement.  The requirement may be applied by a special condition.

§ 23.977(a)(2) -- Fuel Tank Outlet

The strainer size must be appropriate for the aircraft diesel engine fuel requirements, especially considering eliminating the possibility of injector and pump contamination.  The airplane should comply with the requirements of § 23.977(a)(2) in lieu of § 23.977(a)(1).  The requirement may be applied by a special condition.

§ 23.991 -- Fuel Pumps,

§ 23.993 -- Fuel System Lines and Fittings,

§ 23.994 -- Fuel System Components,

§ 23.995 -- Fuel Valves and Controls,

§ 23.997 -- Fuel Strainer or Filter

Fuel system components designed for small airplanes may be optimized or designed for low-pressure gasoline systems.  Components that will be exposed to the effects of high-pressure pumps will need to be designed to account for the effects of high pressure and fatigue, perhaps similar to requirements for hydraulic systems.  Turbine fuels may have additives added after they are refined that modify fuel properties associated with airplane icing, biological contamination, static buildup, flow improvement, weathering, and temperature stability.  Frequently, it cannot be determined if these additives are in the fuel that is delivered to the airplane.

Over-wing fueling systems at airports may not have the same source as pressure fueling systems for large transport airplanes and may contain different additives.  Determine whether the aircraft fuel system components are compatible with the fuel and with any potential additive that could be introduced into the fuel.

The military are utilizing some additives to increase the thermal stability of jet fuels that are not commercially utilized.  The potential effects of these additives on the systems of small airplanes will need to be examined if there is any possibility of the airplane being operated on military fuels.  In addition to material properties, the effects on fuel gauging systems, and the effects on filtering systems/media will need to be specifically evaluated.

Kerosene fuels can potentially produce an explosive or flammable mixture in the fuel tanks at normal operating temperatures while gasoline mixtures in the fuel tanks are typically beyond the rich limit.  Fuel tank ignition sources need to be eliminated over the total life cycle of the airplane, and extreme care should be used when converting the fuel system of an airplane from gasoline to kerosene-based fuels.  Grounding of all metal components within the fuel tank is perhaps more important with diesel powered engines (relative to gasoline) to ensure common potential (and, therefore, no arcing) between the metal components and the inrushing fuel, which is something to consider in STC re-engine projects.  Also, re-evaluation of fuel quantity indicating systems for compatibility, ignition source, and marking requirements should be considered.

In some ground-based diesel engine designs, fuel line pressures have been known to exceed 3,000 psi, which is significantly higher than conventional turbine engine fuel systems.  Extra attention should be given to fuel system components and the instructions for continued airworthiness for the system and its components.  Basic compliance addressing the specific design challenges of the aircraft diesel engine systems will be adequate.

§ 23.1145 -- Ignition Switches

This requirement will have to be modified to incorporate an appropriate means of stopping the engine.  In place of the basic requirement, there must be a means to stop the engine; this may mean shutting off the engine control (FADEC, or similar) or appropriate components.  Depending on specific system details, a special condition, exemption or ELOS for § 23.1145 could be utilized.

As the diesel engine is a compression ignition engine, the ignition source is the heat created by compressing the air-fuel mixture in the cylinder.  Section 23.1145(a) would not be applicable.  Part of the intent of § 23.1145(b) is to have a method available to the crew to quickly stop an engine(s).  As a diesel engine does not have an ignition system, an alternate means of rapidly stopping an engine(s) would need to be provided and addressed via a special condition, exemption or ELOS.

§ 23.1165 – Engine Ignition Systems (Permanent electrical power)

Modern diesel engines will most likely be equipped with EEC or FADEC.  These systems need permanent electrical power. Battery ignition systems are addressed in § 23.1165.  The need for permanent electrical power is identical to the EEC/FADEC Electrical Power requirement.  The EEC/FADEC system will have the same critical function as the battery ignition system identified in § 23.1165.  This requirement will need to be addressed via a special condition or ELOS.

Since the electronic engine control without mechanical backup requires permanent electric power, the criticality of the power supply system may be higher than on a conventional magneto ignition system.  The § 23.1309 assessment (FHA and FMEA) has to address this failure mode.  If the electric power after loss of generator is limited to a specific time (e.g., if supplied by battery), this remaining time should be demonstrated and the information should be in the POH.  The time required in § 23.1353(h) may not establish the same level of safety as a conventional magneto ignition system.  In any case, the pilot should be informed that the engine will stop if the electric power is lost (POH).

§ 23.1203(a)(1)(ii) -- Fire Detector System

If the aircraft diesel engine is installed on a multi-engine airplane and the engine utilizes turbochargers, this section will apply.  Basic compliance is adequate.

#### Subpart F -- Equipment

§ 23.1305 -- Powerplant Instruments

The installation of an aircraft diesel engine will be in accordance with the engine's installation manual and operated within the requirements of its TC.  The instrumentation requirements in § 23.1305 were written for conventional reciprocating engines and turbine engines.  The requirement did not envision the use of aircraft diesel engines.  In addition, instrumentation may be determined necessary for a particular installation that is not specified in the current requirements or the engine's installation manual.  Should the aircraft diesel engine limiting parameters be different than those specified in § 23.1521, special conditions will most likely be developed to require those parameters to be used as limitations (see § 23.1521).  The limiting parameters will be displayed in the instrument panel as required by § 23.1305.  Also, see § 23.1521 for fuel temperature limitations.

Special conditions will most likely be developed if any additional items to those specified in § 23.1305(b), or items described under § 23.1305, paragraphs (c), (d), or (e), are required.

Any deletions from the parameters required by § 23.1305(b) could be administered via an exemption through the development of an equivalent level of safety or in combination with any special conditions requiring additional parameters.

Subpart G -- Operating Limitations and Information

§ 23.1521 -- Powerplant Limitations

General Comment:  An aircraft diesel engine may have different critical parameters than conventional reciprocating engines.  Should the aircraft diesel engine limiting parameters be different than those specified in § 23.1521, special conditions will most likely be developed to require those parameters to be used as limitations.  Also see the discussion for § 23.1305.

Section 23.1521(d) requires minimum fuel grades in order for the engine to be operated within the limitations of § 23.1521, paragraphs (b) and (c).  It is a general opinion that Jet A will be the fuel of choice.  Fuel grade designations are applicable to aviation gasolines and, therefore, are not appropriate for aircraft diesel engines.  The intent of the requirement is clear; however, the turbine engine “fuel designation” is more applicable for this section.

Fuel gelling or freezing has not been a concern with airplanes operating on gasoline fuels; however, kerosene fuels will freeze or gel at ambient temperatures much higher than gasoline fuels.  The CRC fuel properties handbook shows the specification limit freezing point for Jet-A fuel as –40C, with the typical kinematic viscosity of 10 centistokes at the freezing point.  An airplane operating on kerosene fuels should have some means of ensuring that the fuel in the tanks stays in the liquid state during operations.  Fuel gelling or freezing is a special concern for small airplanes; smaller fuel tanks will cool much quicker than transport-sized fuel tanks.

The most common method of heating turbine fuel has been through motive fuel being returned into the fuel tanks.  This method can often be shown to heat the fuel to an adequate temperature so that the danger of fuel freezing or gelling is avoided.

If the fuel in the tanks cannot be shown to flow suitably under all temperature conditions, then fuel temperature limitations will be required.  For the different types of fuels (Kerosene (Jet) Fuel and Diesel car fuel), different temperature limitations may be necessary.  If both fuels are used at the same time, the fuel temperature limit may be unclear.  This is the case if the pilot does not know the type of the fuel; therefore, the worst limitation has to be used. Clear and unambiguous information will have to be in the Airplane Flight Manual (AFM).  The temperature limitations would be considered as part of the essential operating parameters for an airplane with an engine that operates on kerosene-based fuels, and these limitations will be mandated as operating limitations on the TCDS and in the Airplane Flight Manual (AFM).

(1) The take-off temperature limitation will be determined by testing to determine the minimum cold-soaked temperature at which the airplane can operate.

(2) The minimum operating temperature limitation will be determined by testing to determine the minimum operating temperature acceptable after take off from the minimum take-off temperature established in (1).

Analysis should be avoided as testing is preferred in establishing these limitations, similar to hot fuel testing in an overall systems test.  If low temperature operating limits are not established by testing, then the airplane will be temperature limited.  The temperature limit is set by establishing the temperature where the specified fuel gels, by evaluating any limiting viscosity effects of the fuel at the cold temperatures, and by adding an appropriate temperature margin above any limiting temperature.  The temperature margin will be necessary to account for the variations in fuel properties in order to allow adequate fuel flow at the limiting temperature.  This requirement (depending upon how it is implemented) could also impose the need for a fuel temperature display.

Section 23.1521(e) will probably need to be replaced by a special condition requiring the establishment of maximum and minimum operating temperatures, as discussed above, for any airplane powered by a diesel engine.

§ 23.1557(c)(1)(ii) -- Miscellaneous Markings and Placards

The airplane will comply with the provisions of § 23.1557(c)(1)(ii) in lieu of § 23.1557(c)(1)(i).  A special condition would most likely be needed to require these changes.

Inadvertent over-wing fueling with gasoline is also a possibility that should be minimized.  An additional warning placard stating the following (or similar) should be placed nearby or integrated with the placard required by § 23.1557(c)(1)(ii), and the engine TCDS fuels should be listed:

EXAMPLE:

“WARNING

THIS AIRPLANE IS EQUIPPED WITH A

COMPRESSION IGNITION  (DIESEL) ENGINE

###### SERVICE WITH APPROVED FUELS LISTED BELOW ONLY

JET A

JET A1

##### DIESEL #2”

A special condition will most likely be needed to require the placard.

## Effect of Policy

The general policy stated in this document does not constitute a new regulation or create what the courts refer to as a "binding norm".  The office that implements policy should follow this policy when applicable to the specific project.  Whenever an applicant's proposed method of compliance is outside this established policy, it must be coordinated with the policy issuing office, e.g., through the issue paper process or equivalent.

Applicants should expect that the certificating officials will consider this information when making findings of compliance relevant to new certificate actions.  Also, as with all advisory material, this policy statement identifies one means, but not the only means, of compliance.

Conclusion

The Small Airplane Directorate has determined that all proposed diesel engine installations, whether supplemental, amended or new TC projects, will be significant as defined in Order 8100.5.  As such, the ACO is expected to notify the Standards Office of such projects promptly and forward certification project notifications and associated certification plans as soon as practical after project application.  The ACO will identify the technological areas of concern identified in this policy paper, as well as any additional concerns and develop a G-1 issue paper to establish the certification basis.  Signature authority for certificate issuance on these projects is retained by the Standards Office and will be redelegated on a case-by-case basis as this new technology is understood and integrated into aerospace products.

S/ Dorenda Baker

for

Michael Gallagher

Manager, Small Airplane Directorate

Aircraft Certification Service

Distribution:

Manager, Aircraft Engineering Division, AIR-100

Manager, Brussels Aircraft Certification Staff, AEU-100

Manager, Boston Aircraft Certification Office, ANE-150

Manager, New York Aircraft Certification Office, ANE-170

Manager, Ft. Worth Airplane Certification Office, ASW-150

Manager, Special Certification Office, ASW-190

Manager, Atlanta Aircraft Certification Office, ACE-115A

Manager, Chicago Aircraft Certification Office, ACE-115C

Manager, Wichita Aircraft Certification Office, ACE-115W

Manager, Anchorage Aircraft Certification Office, ACE-115N

Manager, Seattle Aircraft Certification Office, ANM-100S

Manager, Denver Aircraft Certification Office, ANM-100D

Manager, Los Angeles Aircraft Certification Office, ANM-100L