| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 13 to Document 10-E |
|  | 17 May 2007 |
|  | Original: English |
| EUROPEAN COMMON PROPOSALS FOR THE WORK OF THE CONFERENCE |
| PART 13 |
| Agenda item 1.13 |

1.13	taking into account Resolutions 729 (WRC-97), 351 (WRC-03) and 544 (WRC-03), to review the allocations to all services in the HF bands between 4 MHz and 10 MHz, excluding those allocations to services in the frequency range 7 000-7 200 kHz and those bands whose allotment plans are in Appendices 25, 26 and 27 and whose channelling arrangements are in Appendix 17, taking account of the impact of new modulation techniques, adaptive control techniques and the spectrum requirements for HF broadcasting

sub-part 13a

Resolution 351

Introduction

This sub-part addresses only Resolution 351.

It is proposed to modify the Part A of Appendix 17 in order to reduce the actual frequencies for NBDP to the GMDSS requirement (see Appendix 15), to release the rest of the majority of the frequencies for the possible use for data transmission using digital technology (e.g. see Recommendation ITU-R M.[HF DATA]) in the maritime mobile service, including the bands for Morse frequencies.

In Part B of Appendix 17 changes are proposed accordingly to Part A. The section dealing with Morse frequencies are candidates for suppression due to the new utilization proposed above. The spectrum remains available for the maritime mobile service.

In Part B, Section I Radiotelephony, it is proposed to add a note authorizing the administrations to notify assignments to stations in the maritime mobile service other than those using radiotelephony.

The proposals for this ECP are fully in line with the CPM text method C for Agenda item 1.13.

APPENDIX  17  (Rev.WRC-03)

Frequencies and channelling arrangements in the
high-frequency bands for the maritime mobile service

(See Article 52)

MOD	EUR/10A13/1

PART  A  –  Table of subdivided bands     (WRC-07)

In the Table, where appropriate1, the assignable frequencies in a given band for each usage are:

–	indicated by the lowest and highest frequency, in heavy type, assigned in that band;

–	regularly spaced, the number of assignable frequencies ( f.) and the spacing in kHz being indicated in italics.

Table of frequencies (kHz) to be used in the band between 4 000 kHz and 27 500 kHz
allocated exclusively to the maritime mobile service

| Band (MHz) | 4 | 6 | 8 | 12 | 16 | 18/19 | 22 | 25/26 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Limits (kHz) | 4 063 | 6 200 | 8 195 | 12 230 | 16 360 | 18 780 | 22 000 | 25 070 |
| Frequencies assignable to ship stations for oceanographic data transmission c) | 4 063.3 to 4 064.8 6 f. 0.3 kHz |  |  |  |  |  |  |  |
| Limits (kHz) | 4 065 | 6 200 | 8 195 | 12 230 | 16 360 | 18 780 | 22 000 | 25 070 |
| Frequencies assignable to ship stations for telephony, duplex operation a) i) p) | 4 066.4 to 4 144.4 27 f. 3 kHz | 6 201.4 to 6 222.4 8 f. 3 kHz | 8 196.4 to 8 292.4 33 f. 3 kHz | 12 231.4 to 12 351.4 41 f. 3 kHz | 16 361.4 to 16 526.4 56 f. 3 kHz | 18 781.4 to 18 823.4 15 f. 3 kHz | 22 001.4 to 22 157.4 53 f. 3 kHz | 25 071.4 to 25 098.4 10 f. 3 kHz |
| Limits (kHz) | 4 146 | 6 224 | 8 294 | 12 353 | 16 528 | 18 825 | 22 159 | 25 100 |

Table of frequencies (kHz) to be used in the band between 4 000 kHz and 27 500 kHz
allocated exclusively to the maritime mobile service (continued )

| Band (MHz) | 4 | 6 | 8 | 12 | 16 | 18/19 | 22 | 25/26 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Limits (kHz) | 4 146 | 6 224 | 8 294 | 12 353 | 16 528 | 18 825 | 22 159 | 25 100 |
| Frequencies assignable to ship stations and coast stations for telephony, simplex operation a) p) | 4 147.4 to 4 150.4 2 f. 3 kHz | 6 225.4 to 6 231.4 3 f. 3 kHz | 8 295.4 to 8 298.4 2 f. 3 kHz | 12 354.4 to 12 366.4 5 f. 3 kHz | 16 529.4 to 16 547.4 7 f. 3 kHz | 18 826.4 to 18 844.4 7 f. 3 kHz | 22 160.4 to 22 178.4 7 f. 3 kHz | 25 101.4 to 25 119.4 7 f. 3 kHz |
| Limits (kHz) | 4 152 | 6 233 | 8 300 | 12 368 | 16 549 | 18 846 | 22 180 | 25 121 |
| Frequencies assignable to ship stations for wide-band telegraphy, facsimile and special transmission systems p) | 4 154 to 4 170 5 f. 4 kHz | 6 235 to 6 259 7 f. 4 kHz | 8 302 to 8 338 10 f. 4 kHz | 12 370 to 12 418 13 f. 4 kHz | 16 551 to 16 615 17 f. 4 kHz | 18 848 to 18 868 6 f. 4 kHz | 22 182 to 22 238 15 f. 4 kHz | 25 123 to 25 159 10 f. 4 kHz |
| Limits (kHz) | 4 172 | 6 261 | 8 340 | 12 420 | 16 617 | 18 870 | 22 240 | 25 161.25 |
| Frequencies assignable to ship stations for oceanographic data transmission c) |  | 6 261.3 to 6 262.5 5 f. 0.3 kHz | 8 340.3 to 8 341.5 5 f. 0.3 kHz | 12 420.3 to 12 421.5 5 f. 0.3 kHz | 16 617.3 to 16 618.5 5 f. 0.3 kHz |  | 22 240.3 to 22 241.5 5 f. 0.3 kHz |  |
| Limits (kHz) | 4 172 | 6 262 | 8 341.75 | 12 421.75 | 16 618.75 | 18 870 | 22 241.75 | 25 161.25 |
| Frequencies assignable to ship stations for wide-band telegraphy, facsimile and special transmission systems p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 176 | 6 266 | 8 341.75 | 12 421.75 | 16 618.75 | 18 870 | 22 241.75 | 25 161.25 |
| Frequencies (paired) assignable to ship stations for narrow-band direct-printing (NBDP) telegraphy and data transmission systems at speeds not exceeding 100 Bd for FSK and 200 Bd for PSK d) j) | 4 176.5 to 4 179 5 f. 0.5 kHz | 6 266.5 to 6 270 7 f. 0.5 kHz |  |  |  |  |  |  |
| Limits (kHz) | 4 179.25 | 6 270.25 | 8 341.75 | 12 421.75 | 16 618.75 | 18 870 | 22 241.75 | 25 161.25 |
| Frequencies assignable to ship stations for data transmission m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 186.75 | 6 284.75 | 8 341.75 | 12 421.75 | 16 618.75 | 18 870 | 22 241.75 | 25 161.25 |

Table of frequencies (kHz) to be used in the band between 4 000 kHz and 27 500 kHz
allocated exclusively to the maritime mobile service (continued )

| Band (MHz) | 4 | 6 | 8 | 12 | 16 | 18/19 | 22 | 25/26 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Limits (kHz) | 4 186.75 | 6 284.75 | 8 341.75 | 12 421.75 | 16 618.75 | 18 870 | 22 241.75 | 25 161.25 |
| Frequencies assignable to ship stations for data transmission h) m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 202.25 | 6 300.25 | 8 376.25 | 12 476.75 | 16 683.25 | 18 870 | 22 284.25 | 25 172.75 |
| Frequencies (paired) assignable to ship stations for NBDP telegraphy and data transmission systems at speeds not exceeding 100 bauds for FSK and 200 bauds for PSK d) j) |  |  | 8 376.5 to 8 381 10 f. 0.5 kHz |  |  |  |  |  |
| Limits (kHz) | 4 202.25 | 6 300.25 | 8 381.25 | 12 476.75 | 16 683.25 | 18 870 | 22 284.25 | 25 172.75 |

Table of frequencies (kHz) to be used in the band between 4 000 kHz and 27 500 kHz
allocated exclusively to the maritime mobile service (continued )

| Band (MHz) | 4 | 6 | 8 | 12 | 16 | 18/19 | 22 | 25/26 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Limits (kHz) | 4 202.25 | 6 300.25 | 8 381.25 | 12 476.75 | 16 683.25 | 18 870 | 22 284.25 | 25 172.75 |
| Frequencies assignable to ship stations for data transmission m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 202.25 | 6 300.25 | 8 396.25 | 12 516.75 | 16 693.25 | 18 892.75 | 22 351.75 | 25 192.75 |
| Frequencies (paired) assignable to ship stations for NBDP telegraphy and data transmission systems at speeds not exceeding 100 bauds for FSK and 200 bauds for PSK d) j) |  |  |  | 12 517 to 12 521.5 10 f. 0.5 kHz | 16 693.5 to 16 698 10 f. 0.5 kHz |  |  |  |
| Limits (kHz) | 4 202.25 | 6 300.25 | 8 396.25 | 12 522 | 16 698.5 | 18 892.75 | 22 351.75 | 25 192.75 |
| Frequencies assignable to ship stations for data transmission m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 202.25 | 6 300.25 | 8 396.25 | 12 559.75 | 16 784.75 | 18 892.75 | 22 351.75 | 25 192.75 |
| Frequencies (non paired) assignable to ship stations for data transmission systems m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 207.25 | 6 311.75 | 8 414.25 | 12 576.75 | 16 804.25 | 18 898.25 | 22 374.25 | 25 208.25 |
| Frequencies assignable to ship stations for digital selective calling k) l) | 4 207.5 to 4 209 4 f. 0.5 kHz | 6 312 to 6 313.5 4 f. 0.5 kHz | 8 414.5 to 8 416 4 f. 0.5 kHz | 12 577 to 12 578.5 4 f. 0.5 kHz | 16 804.5 to 16 806 4 f. 0.5 kHz | 18 898.5 to 18 899.5 3 f. 0.5 kHz | 22 374.5 to 22 375.5 3 f. 0.5 kHz | 25 208.5 to 25 209.5 3 f. 0.5 kHz |
| Limits (kHz) | 4 209.25 | 6 313.75 | 8 416.25 | 12 578.75 | 16 806.25 | 18 899.75 | 22 375.75 | 25 210 |
| Limits (kHz) | 4 209.25 | 6 313.75 | 8 416.25 | 12 578.75 | 16 806.25 | 19 680.25 | 22 375.75 | 26 100.25 |
| Frequencies assignable to coast stations for data transmission m) n) o) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 213.75 | 6 317.25 | 8 416.25 | 12 619.25 | 16 816.75 | 19 703.25 | 22 443.75 | 26 120.75 |

Table of frequencies (kHz) to be used in the band between 4 000 kHz and 27 500 kHz
allocated exclusively to the maritime mobile service (end)

| Band (MHz) | 4 | 6 | 8 | 12 | 16 | 18/19 | 22 | 25/26 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Limits (kHz) | 4 213.75 | 6 317.25 | 8 416.25 | 12 619.25 | 16 816.75 | 19 703.25 | 22 443.75 | 26 120.75 |
| Frequencies (paired) assignable to coast stations for NBDP and data transmission systems, at speeds not exceeding 100 Bd for FSK and 200 Bd for PSK d) n) o) | 4 214 to 4 216.5 7 f. 0.5 kHz | 6 317.5 to 6 321 9 f. 0.5 kHz | 8 416.5 to 8 421 10 f. 0.5 kHz | 12 619.5 to 12 623.5 10 f. 0.5 kHz | 16 817 to 16 821 10 f. 0.5 kHz |  |  |  |
| Limits (kHz) | 4 216.75 | 6 321.25 | 8 421.25 | 12 623.75 | 16 821.25 | 19 703.25 | 22 443.75 | 26 120.75 |
| Frequencies assignable to coast stations for data transmission m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 219.25 | 6 330.75 | 8 436.25 | 12 656.75 | 16 902.75 | 19 703.25 | 22 443.75 | 26 120.75 |
| Frequencies assignable to coast stations for digital selective calling l) | 4 219.5 to 4 220.5 3 f. 0.5 kHz | 6 331 to 6 332 3 f. 0.5 kHz | 8 436.5 to 8 437.5 3 f. 0.5 kHz | 12 657 to 12 658 3 f. 0.5 kHz | 16 903 to 16 904 3 f. 0.5 kHz | 19 703.5 to 19 704.5 3 f. 0.5 kHz | 22 444 to 22 445 3 f. 0.5 kHz | 26 121 to 26 122 3 f. 0.5 kHz |
| Limits (kHz) | 4 221 | 6 332.5 | 8 438 | 12 658.5 | 16 904.5 | 19 705 | 22 445.5 | 26 122.5 |
| Frequencies assignable to coast stations for wide-band, facsimile, special and data transmission systems and direct-printing telegraphy systems m) p) |  |  |  |  |  |  |  |  |
| Limits (kHz) | 4 351 | 6 501 | 8 707 | 13 077 | 17 242 | 19 755 | 22 696 | 26 145 |
| Frequencies assignable to coast stations for telephony, duplex operation a) p) | 4 352.4 to 4 436.4 29 f. 3 kHz | 6 502.4 to 6 523.4 8 f. 3 kHz | 8 708.4 to 8 813.4 36 f. 3 kHz | 13 078.4 to 13 198.4 41 f. 3 kHz | 17 243.4 to 17 408.4 56 f. 3 kHz | 19 756.4 to 19 798.4 15 f. 3 kHz | 22 697.4 to 22 853.4 53 f. 3 kHz | 26 146.4 to 26 173.4 10 f. 3 kHz |
| Limits (kHz) | 4 438 | 6 525 | 8 815 | 13 200 | 17 410 | 19 800 | 22 855 | 26 175 |

NOC

Note a)

SUP	EUR/10A13/2

Note b)

NOC

Notes c) and d).

SUP	EUR/10A13/3

Note e)

SUP	EUR/10A13/4

Note f)

SUP	EUR/10A13/5

Note g)

NOC

Notes h) to l).

MOD	EUR/10A13/6

m)	Frequencies from these frequency bands may also be used for A1A or A1B Morse telegraphy subject to not claiming protection from other stations in the maritime mobile service using data transmissions.

NOC

Notes n) and o)

MOD	EUR/10A13/7

p)	These sub-bands, except the frequencies referred to in Notes i), j), n) and o), could be used for digital technologies for maritime mobile service (e.g. as described in Recommendation ITU-R M.[HF DATA]).

Reasons:	See introduction.

PART  B  –  Channelling arrangements

Section I  –  Radiotelephony

ADD	EUR/10A13/8

6	d)	The channelling arrangement specified in the Sub-Sections A and B does not prejudice the rights of administrations to establish, and to notify, assignments to stations in the maritime mobile service other than those using radiotelephony, provided that:

–	the occupied bandwidth does not exceed 2 800 Hz and is situated wholly within one frequency channel.     (WRC-07)

Reasons:	This will allow the use of digital technology by the administrations within the maritime radiotelephone for coast and ship stations. Consequential changes might be needed in relevant parts of the Radio Regulations.

Section II  –  Narrow-band direct-printing telegraphy (paired frequencies)

MOD	EUR/10A13/9

Table of frequencies for two-frequency operation by coast stations (kHz)

| Channel | 4 MHz band 1 | 6 MHz band 3 | 8 MHz band 4 |
| --- | --- | --- | --- |
| No. | Transmit | Receive | Transmit | Receive | Transmit | Receive |
| 1 2 3 4 5 |  |  |  |  | 8 376.5 2 8 417 8 417.5 8 418 8 418.5 | 8 376.5 2 8 377 8 377.5 8 378 8 378.5 |
| 6 7 8 9 10 | 4 214 4 214.5 4 215 | 4 176 4 176.5 4 177 | 6 317.5 6 318 6 318.5 6 319 | 6 266 6 266.5 6 267 6 267.5 | 8 419 8 419.5 8 420 8 420.5 8 421 | 8 379 8 379.5 8 380 8 380.5 8 381 |
| 11 12 13 14 15 | 4 177.5 2 4 215.5 4 216 4 216.5 | 4 177.5 2 4 178 4 178.5 4 179 | 6 268 2 6 319.5 6 320 6 320.5 6 321 | 6 268 2 6 268.5 6 269 6 269.5 6 270 |  |  |
| 16 17 18 19 20 |  |  |  |  |  |  |
| 21 22 23 24 25 |  |  |  |  |  |  |
| 26 27 28 29 30 |  |  |  |  |  |  |
| 31 32 33 34 35 |  |  |  |  |  |  |
| 36 37 38 39 40 |  |  |  |  |  |  |
| 1 Ship stations may use the coast station receiving frequencies for transmitting A1A or A1B Morse telegraphy (working), with the exception of channel No. 11 (see Appendix 15). 2 For the conditions of use of this frequency, see Article 31. 3 Ship stations may use the coast station receiving frequencies of channel Nos. 25 up to and including 34 for transmitting A1A or A1B Morse telegraphy (working). 4 Ship stations may use the coast station receiving frequencies of channel Nos. 29 up to and including 40 for transmitting A1A or A1B Morse telegraphy (working). |

Table of frequencies for two-frequency operation by coast stations (kHz)

| Channel | 12 MHz band 5 | 16 MHz band 6 |  |
| --- | --- | --- | --- |
| No. | Transmit | Receive | Transmit | Receive |  |  |
| 1 2 3 4 5 |  |  |  |  |  |  |
| 6 7 8 9 10 |  |  |  |  |  |  |
| 11 12 13 14 15 |  |  |  |  |  |  |
| 16 17 18 19 20 |  |  |  |  |  |  |
| 21 22 23 24 25 |  |  | 16 817 16 817.5 16 818 16 695 2 16 818.5 | 16 693.5 16 694 16 694.5 16 695 2 16 695.5 |  |  |
| 26 27 28 29 30 |  |  | 16 819 16 819.5 16 820 16 820.5 16 821 | 16 696 16 696.5 16 697 16 697.5 16 698 |  |  |
| 31 32 33 34 35 |  |  |  |  |  |  |
| 36 37 38 39 40 |  |  |  |  |  |  |
| 41 42 43 44 45 |  |  |  |  |  |  |
| 5 Ship stations may use the coast station receiving frequencies of channel Nos. 58 up to and including 156 for transmitting A1A or A1B Morse telegraphy (working), with the exception of channel No. 87 (see Appendix 15). 6 Ship stations may use the coast station receiving frequencies of channel Nos. 71 up to and including 193 for transmitting A1A or A1B Morse telegraphy (working). |

Table of frequencies for two-frequency operation by coast stations (kHz)

| Channel | 12 MHz band 5 (cont.) |  |
| --- | --- | --- |
| No. | Transmit | Receive |  |  |
| 46 47 48 49 50 |  |  |  |  |
| 51 52 53 54 55 |  |  |  |  |
| 56 57 58 59 60 |  |  |  |  |
| 61 62 63 64 65 |  |  |  |  |
| 66 67 68 69 70 |  |  |  |  |
| 71 72 73 74 75 |  |  |  |  |
| 76 77 78 79 80 |  |  |  |  |
| 81 82 83 84 85 | 12 619.5 12 620 12 620.5 12 621 12 621.5 | 12 517 12 517.5 12 518 12 518.5 12 519 |  |  |
| 86 87 88 89 90 | 12 622 12 520 2 12 622.5 12 623 12 623.5 | 12 519.5 12 520 2 12 520.5 12 521 12 521.5 |  |  |
| 91 92 93 94 95 |  |  |  |  |

SUP	EUR/10A13/10

Section III  –  Narrow-band direct-printing telegraphy 
(non-paired frequencies)

SUP	EUR/10A13/11

Section IV  –  Morse telegraphy (calling)

SUP	EUR/10A13/12

Section V  –  Morse telegraphy (working)

Reasons:	See introduction.

______________

# Footnotes

1 	Within the non-shaded boxes.