November  21, 1997

Contract # TW-0928

SPECIAL SPECIFICATION

SECTION 02935-S

NATIVE GRASS SEEDING

PART 1 - GENERAL	 Page

1.01	Scope	2

1.02	Applicable Standards	2

1.03	Qualifications	2

1.04	Coordination	2

1.05	Submittals	2

1.06	Protection and Maintenance of Native Grasses	3

PART 2 - PRODUCTS

2.01	Seed	4

2.02	Mulch	4

2.03	Fertilizer	4

2.04	Polyacrylamide	5

2.05	Enzymatic Agent	5

2.06	Organic Amendment	5

PART 3 - EXECUTION

3.01	Soil Preparation	7

3.02	Fertilization and Enzyme Application	7

3.03	Seeding & Irrigation	7

3.04	Mulching	8

3.05	Inspection for Native Grasses	8

SPECIAL SPECIFICATION

SECTION 02935-S

NATIVE GRASS SEEDING

PART 1 - GENERAL

1.01	SCOPE

A.	Furnish all labor, materials, and equipment necessary for preparation of seedbed, installation of seed, mulch, and related work specified herein.

1.02 	APPLICABLE STANDARDS

A.	All native grass seed shall be certified by state of origin.  The certification authority for the state of New Mexico is the New Mexico Crop Improvement Association.

1.03	QUALIFICATIONS

A.	All work specified herein shall be performed by a licensed landscape contractor experienced with the type and scale of work required, which includes mulching, and having equipment and personnel adequate to perform the work satisfactorily.

1.04	COORDINATION

A.	Determine the acceptability of subgrade preparation prior to the start of native grass seeding operations.  Protect all existing items to remain and new work of other trades to ensure proper timing of each phase of work.

1.05	SUBMITTALS

A.	Proposed source of all native grass and shrub seed which shall indicate the location from which the seed was harvested.

B.	Sources of supply for mulch and fertilizer.

C.	Seed bag tags and weights per bag and copies of invoices identified by project name.

D.	Submit in accordance with Specification 1300.

1.06	PROTECTION AND MAINTENANCE OF NATIVE GRASSES

A.	General:  Protect and care for seeded areas until final acceptance of the work.  Repair any damage to seeded areas caused by pedestrian or vehicular traffic or vandalism.

B.	Protection and Maintenance of Native Seed in Irrigated Areas:  For areas where temporary irrigation is provided, protect and maintain native seed areas until uniform germination and growth is established.  At that time, the area will be accepted by the SDR if no void  or bare areas greater than 25 square inches occur within the seeded area.  If these standards are not met the area shall be reseeded and maintained until final acceptance.  Remove tumbleweed, Russian Thistle and other nuisance, non-grassy weeds during the maintenance period.

PART 2 - MATERIALS

2.01	SEED

A.	All native grass seed shall be obtained from sources in New Mexico unless proof is provided that a particular seed is unavailable within the state.

B.	Contractor shall furnish certification showing origin of all seed and pure live seed (P.L.S.) purity times percent germination.  Each bag of seed shall be tagged and sealed by the seed dealer in accordance with the State Department of Agriculture or other local certification authority within the state of origin.  The tag or label shall indicate analysis of seed and date of analysis, which shall not be more than 9 months prior to delivery date.  Seed may be premixed by the seed dealer and appropriate data indicated on the bag label for each variety.

C.	The seed mix shall be as follows:

Native Grass Seed

Common Name	Botanical Name	Seeding Rate

Hachita Blue Grama 	Bouteloua Gracilis "Hachita"	4 lbs. PLS/1000 Sq. Ft.

2.02	MULCH

A.	Hydromulch:  Excel Fibermulch with tackifier as manufactured by American Excelsior Co.; 850 Avenue H East, P.O. Box 5067, Arlington, Texas, 76001, (817) 640-1555, local phone (505) 345-7806, or an approved equivalent mulch with tackifier.

B.	Tackifier:  Exact-Tak tackifier as manufactured by American Excelsior Co.; 850 Avenue H East, P.O. Box 5067, Arlington, Texas, 76001, (817) 640-1555, local phone (505) 345-7806, or an approved equivalent tackifier for straw or hay mulch.

C.	Substitutions are allowed only under provisions of section 1600.

2.03	FERTILIZER

A.	Slow release nitrogen:  Provide urea formaldehyde applied at 38 lbs. actual nitrogen per acre.

B.	Fast release nitrogen:  Provide ammonium sulphate applied at 40 lbs. actual nitrogen per acre.

C.	Phosphorous:  Provide P205 (phosphoric acid) applied at the rate of 46 lbs. per acre.

D.	Sulphur:  Provide in water soluble form applied at 48 lbs. per acre.

2.04	POLYACRYLAMIDE:

A.	Provide a granular form of a cross-linked polyacrylamide.  Polyacrylate materials are not acceptable.  The following are considered approved:

Stockosorb 300F:	Organic Technology Inc.

2017 Skyline NE, Suite B

Albuquerque, New Mexico 87123

(505)  291-1100, (505)  291-1400,  Fax (505) 271-1600

Polyacrylamide:		Western Polyacrylamide, Inc.,

P.O. Box 790

Castle Rock, Colorado 80104,

(303) 688-3814

Terra Sorb HB:		American Excelsior

4019 Edith Blvd. N.E.

P.O. Box 6494

Albuquerque, New Mexico 87197

2.05	ENZYMATIC AGENT:

BioMax or SuperBio as available from  :

Organic Technology Inc.

2017 Skyline NE, Suite B

Albuquerque, New Mexico 87123

(505) 291-1100, (505) 291-1400,  Fax (505) 271-1600

or an approved equivalent enzymatic agent.  Apply BioMax or SuperBio at a rate of 5 gallons per acre, diluted with 10 gallons or more of water.

2.06	ORGANIC AMENDMENT:

OMNI  as available from:

Western Organic Inc.

Albuquerque, New Mexico 87125

(505)  877-8670

Apply at a rate of 2" loose depth.

New Mexico Compost is available from:

New Mexico Compost Products

from Soilutions

Compost Site:  9008 Bates Road, SE

Albuquerque, New Mexico  87105

(505) 877-0220

Apply at a rate of 1” loose depth.

PART 3 - EXECUTION

3.01	SOIL PREPARATION

A.	Clear areas for seeding of all debris.  Acceptability of the grades shall be determined by the SDR prior to seed bed preparation.

B.	Prepare the seed bed to a minimum depth of 8 inches by tilling with a plow, ripper, rotovator or disc.  All competitive vegetation, with the exception of existing shrub material (including Chamisa, 4-Wing Salt Bush, and others) shall be uprooted during seed bed preparation and the soil shall be uniformly worked to a  surface free of clods, large stones of over 1/2 inch in any dimension, or other foreign material that would interfere with the seeding operations.

C.	Till cross-linked polyacrylamide into the top 8" of the soil at a rate of 7 pounds per 1000 square feet.  Till in organic amendment into the top 8" of the soil.

D.	Tilling must be performed across the slope when practical and shall be performed in two directions whenever one is insufficient to adequately break up the soil in the SDR's opinion.  Tilling shall not occur when the wind is over 10 mph and is causing a dust problem to adjoining areas.

E.	The extent of seed bed preparation shall not exceed the area on which the entire seeding operation can be accomplished to such prepared seed bed within a 24 hour period.

F.	Use extreme caution when disking near shallow buried irrigation piping.  Repair any piping damaged during disking or seeding operations noted below.

G.	Irrigate prepared soil area for 4 weeks at the rate of 2 cycles/day.  See chart in section 3.03 for run times.  The intent of watering is to sprout all weed seeds in the soil.  Spray all weeds with Round-up or remove all weeds at the end of 4 weeks.  If the area is sprayed with Round-up, wait 2 weeks before seeding.

3.02	FERTILIZATION AND ENZYME APPLICATION

A.	Apply fertilizer  and enzymatic treatment of the type and formulation and rate of application as designated uniformly to the prepared seed bed.

3.03	SEEDING & IRRIGATION

A.	Seeding shall be accomplished only between May 15th and July 1st unless specific permission in writing is issued by the SDR to allow seeding before or after these dates.

B.	Broadcast seeding shall be employed utilizing a rotary spreader or a seeder box with a gear feed mechanism.  Rice hulls and other fillers shall be used to prevent uneven separation of lighter seed.  Immediately following the seeding operation, the seedbed shall be lightly raked or chained to provide approximately 1/2" cover of soil over most of the seed.

C.	Suggested Irrigation Schedule for Installation and Establishment of Blue Grama Native Grass

| Month | Pop up Sprayhead | Gear Driven Head |
| --- | --- | --- |
|  | Cycles/Day |

Run Time of

| Cycle | Cycles/Day | Run Time of Cycle |
| --- | --- | --- |
| April (weed eradication) | 2 | 30 minutes | 2 | 1 hour |

May 15-May 30

(seed

| establishment) | 4 | 30 minutes | 4 | 1 hour |
| --- | --- | --- | --- | --- |
| June | 2 | 30 minutes | 2 | 1 hour |
| July | 2 | 30 minutes | 2 | 1 hour |
| August | 1 | 30 minutes | 1 | 1 hour |
| September | 1 every 3 days | 30 minutes | 1 every 3 days | 1 hour |

3.04	MULCHING

A.	Mulch:  Mulch all seeded areas after seeding operations unless otherwise shown on the drawings. Hydromulch the seeded areas.  All areas are to receive a tackifier.

B.	Hydromulch:  Install with equipment suitable for the task of application of the hydromulch and tackifier and as recommended by the hydromulch manufacturer.  Apply hydromulch with an integral tackifier at a rate of 1,000 pounds per acre.

3.05	INSPECTION FOR NATIVE GRASSES

A.	The following inspection shall be the minimum required inspections to native grass during the course of construction.  Additional inspections shall be made at any time at the discretion of the SDR.

B.	Notify the SDR in writing 48 hours in advance of each required inspection.

C.	The sequence of required inspections shall not be changed from the sequence listed below.  Do not proceed with work of the next sequence without written approval of the work of the previous sequence.  Payment will not be approved for items which have not bee inspected and approved in writing.

1.	Automatic irrigation system where required shall be installed, tested, and approved in accordance with Section 02810.

2.	Each phase of soil preparation shall be inspected in process.

3.	Finish grade shall be inspected.

4.	Seed shall be inspected prior to seeding.

5.	Seeding operations shall be monitored.

6.	Seeded areas shall be inspected after completion.

7.	Seeded areas shall be inspected at the end of the maintenance period.

END OF SECTION