PROPOSAL INSTRUCTIONS:  _X_ DRAFT -- COMMENTS DUE BY:  11/29/06 COB

__ FINAL   -- PROPOSAL DUE BY:  12/15/06 COB

DO TITLE:  EVA Enhanced Right Angle Drive

DO Type:  _ X_ CPFF     ___ FFP

DO Contact Information in Addition to the CRAVE Contract Specialist or CO:

TMR:	Joe Gensler						Phone:  (281) 483-0025

DO Manager:  David Glebe					Phone:  (281) 483-9216

DO Mgr. Alternate:    					Phone:  _____________

Concurrences:

____	                            ____	                            ____

David Glebe 	Harold Reimers	Joe Gensler

DO Manager			      DO Mgr. Management		COTR

____	                            ____	                            ____

Joe Gensler	Steve Miller	Mary F. Thomas

Division TMR		      S & MA				Contract Specialist

Task Contains Flight Hardware, Flight Software or GSE?   	_ X_ Yes	___No

Program Supported:    	_X_Shuttle     _X ISS	 _X_EVA    _ _Advanced

---------------------------------------------------------------------------------------------------------------

WBS:  _X_ 1.0 EVA  __ 2.0 FCE   __ 3.0 EVR   __ ECLSS   __ 5.0 ATCS   __ 6.0 CHeCS

For purposes of complying with FAR 52.232-22, Limitation of Funds, the total amount allotted by the Government to contract is specified in clause B.6, Contract Funding.  The funding listed in B.6 is the amount allotted for all Delivery Orders on the contract combined.

All terms and conditions of the contract apply to this Delivery Order.  In the event of a conflict between the contract and this Delivery Order, the contract shall prevail.

WBS reporting shall be done in accordance with applicable WBS reporting categories, as shown above and in the contract within Section C, Table 1.

# Narrative Task Description

## Background / Problem Description:

- Objective

The existing bilateral tool Right Angle Drive (P/N SEG33106925-305) has revealed early cycle life issues that restrict the useful life and impact overall confidence in the output torque values.  Design, develop, certify, manufacture, and deliver an Enhanced Right Angle Drive (ERAD) that is suitable for breaking and applying static torques and to use as a continuous torque transmission device.

- Need for an Enhanced Right Angle Drive

The Right Angle Drive (P/N: SEG33106925-305) that is currently being used in International Space Station (ISS) assembly tasks was only designed to remove ninety-six (96) bolts that would require no more than five (5) turns each.  Since the RADs initial certification, ISS assembly teams have determined that the RAD needs to be used in other assembly tasks that include driving bolts in excess of five (5) turns as well as performing final bolt torques.  Thus, a new “enhanced” right angle drive is required to complete ISS assembly tasks.

- Prior Work

NASA currently uses a Right Angle Drive (P/N: SEG33106925-301/-303/-305) that was not designed to be used as a transmission to continuously drive bolts more than five (5) turns.  The current design was extensively fit checked to worksites (at the vendor facilities) throughout the development of ISS.  The existing RAD dimensions are believed to be acceptable for the RAD to be used in all assembly tasks which require the use of the RAD.

## Task Description:

The contractor is to perform the necessary analysis and design of the ERAD to meet the performance requirements as listed below.  The contractor shall present a design concept to NASA prior to being awarded the contract to design, fabricate, and certify the ERAD.  Upon approval of the design by NASA, the contractor shall complete the design, fabrication, testing, and certification of the ERAD.  The design shall comply with applicable EVA GDRD requirements.  The contractor shall, upon successful completion of testing, manufacture, and certification, deliver one (1) qualification, five (5) flight, no (0) Neutral Buoyancy Laboratory (NBL) compatible ERADs and provide sustaining engineering as required for the hardware for a period of no less than two (2) years.  No part of the design will be proprietary and NASA will have full access and ownership of all engineering drawings, CAD models, procedures, and related documentation.  The drawings will be released in the Electronic Drawing Control Center.  All drawings will use JSC standard processing (i.e., PRC) callouts.  All documentation (requirements documents, assembly procedures, etc) will be released through the JSC document system.

- Requirements

The ERAD shall meet, at minimum, the requirements that are listed in JSC-33601, Revision J for the Right Angle Drive (P/N: SEG33106925-305) with the following exceptions:

Weight

- The weight of the ERAD shall not exceed 2.8 pounds.

Dimensions

- The ERAD shall not exceed the following envelope dimensions:

  - Stowed (handle closed): 10.83 in. x 2.5 in. x 3.10 in.

  - Deployed (handle extended): 10.83 in. x 2.5 in. x 7.25 in.

- Additional envelope dimension constraints:

  - The output housing of the ERAD should not exceed 1.5 inches in diameter

Interfaces

The enhanced right angle drive (ERAD) shall interface with the following: EVA standard 3/8” male drives and EVA standard female drop proof tethers (DPTs).  These interfaces shall function with a maximum 100(F differential over the operational temperature range.

- Extravehicular Activity Standard 3/8” Male Drive Interface

  - Orientation

    - Interface of the ERAD EVA standard 3/8” male drive to the DPT shall be independent of orientation.

  - Interface Definition

    - Interface to the ERAD EVA standard 3/8” male drive shall be in accordance with ICD JSC-33546 (CTSD-SS-1035).

  - 3/8” Drive Gage

    - The ERAD output drive shall interface with the 3/8” male drive go and no-go gage (SDG38114280-001).

- Drop Proof Tether (DPT) Interface

  - Orientation

    - Interface of the ERAD DPT to the EVA standard 3/8” male drive shall be independent of orientation.

  - Interface Definition

    - Interface of the ERAD DPT shall be in accordance with ICD JSC-33546 (CTSD-SS-1035).

  - Drop Proof Tether Gage

    - The ERAD DPT shall interface with the DPT go and no-go gage (SDG38114281-001) and the McTether load fixture (gage) (SDG38114296-001).

- Push-In-Place (PIP) Pin Interface

  - Interface Definition

    - Interface to the standard 3/16” PIP pin shall be in accordance with ICD JSC-33546 (CTSD-SS-1035).

  - Push-In-Place (PIP) Pin Gage

    - The ERAD DPT shall interface with the DPT PIP pin gage (SDG38114295-001).

Life Cycling of ERAD Mechanism

- Drive Mechanism Cycling

  - The total number of output cycles are derived as follows :

    - 2 drive tasks/EVA x 10 cycles/drive task x 31 EVAs/year x 15 years x F.S. [where F.S. = 2.0] = 18,600 cycles

  - The 3/8” male drive shall be capable of withstanding (at minimum) 18,600 cycles to verify life expectancy.  A cycle is defined as one clockwise (CW) turn followed by one counterclockwise (CCW) turn.  (NOTE: it is acceptable to perform (for acceptance/qualification testing) large number of cycles as follows: 100 CW cycles followed by 100 CCW cycles.)

    - CCW: Break bolt torque with a 28.1 ft-lbs (25.5 ft-lbs x 1.10) ERAD input load

    - CCW: Drive bolt 100 turns with a bolt running torque (ERAD output load) of 2.0 ft-lbs.

    - CW: Drive bolt 100 turns with an bolt running torque (ERAD output load) of 2.0 ft-lbs.

    - CW: Final bolt torque with a 28.1 ft-lbs (25.5 ft-lbs x 1.10) ERAD input load.

  - The above cycle profile (100 cycles) shall be repeated until the required number of cycles are achieved.

  - Life cycle testing may be interrupted to allow the ERAD to cool

- Male Drive Cycling

  - The ERAD male drive shall be capable of withstanding 1860 cycles to verify life expectancy (1 tool change out/task x 2 tasks/EVA x 31 EVAs/year x 15 years x F.S. [where F.S. = 2.0].

- Drop Proof Tether (DPT) Mechanism

  - The DPT drive shall be capable of withstanding 5580 cycles to verify life expectancy (3 DPT change outs/task x 2 tasks/EVA x 31 EVAs/year x 15 years x F.S. [where F.S. = 2.0].

- Handle Deployment Cycling

  - The handle shall be capable of withstanding 1860 cycles to verify life expectancy (1 handle deployment/task x 2 tasks/EVA x 31 EVAs/year x 15 years x F.S. [where F.S. = 2.0]).

Loads

- The ERAD shall be able to meet all of the load and cycle requirements over the full operational temperature range of it's certification.

- The design/analysis/testing of the ERAD shall include thermal degradation factors based on the predicted temperature range of the ERAD.

- At the end of the useful life of useful life of the ERAD, the torque transmission efficiency shall not be less than 1.5:1 (output: input) for both static and dynamic load conditions.

- Torque multiplication factor cannot change by more than 0.4 over the life of the tool.  This may be described by the equation (beginning of life - end of life < .4).

- The rotational input speed (at no-load conditions) shall not exceed sixty (60) revolutions per minute (RPM).

- The rotational input speed shall not exceed sixty (60) RPM when the output torque is driving a bolt with a two (2.0) foot-pound (ft-lb) running torque.

- The maximum input static load shall not exceed 36.6 ft-lbs (30.5 ft-lbs x 1.20).

- The maximum dynamic input load shall not exceed 28.1 ft-lbs (25.5 ft-lbs x 1.10).

  - The cooling time shall be determined through thermal analysis and/or testing but shall not exceed five (5) minutes based on EVA environments extremes

- The ERAD shall be designed such that no debris (i.e., Foreign Object Debris [FOD]) will be generated during the life of the tool

Operational Forces

- The retention force of the DPT locked on an EVA standard 3/8” male drive shall be 18.0 pounds (limit) without functional degradation of the system components.  The DPT shall retain an EVA standard 3/8” male drive for a minimum of 60.0 pounds (ultimate).

- 3/8” Male Drive Soft Docking Force

  - The force required to soft dock into a DPT shall measure between 0.5 and 2.5 pounds.

- Handle Actuation Force

  - The force required to open/close the ERAD handle shall measure between 1.0 and 6.0 pounds (measured at the center of the handle).

- PIP Pin Actuation Force

  - The force required to insert or remove the PIP pin into or out of the ERAD DPT shall measure between 0.25 and 3.5 pounds.

Functional Requirements

- Fastener Installation and Removal

  - ERAD shall be capable of performing breaking torque on fasteners, driving the fastener (during installation or removal), and performing final fastener torque.

- Drive Mechanism Capability

  - The ERAD shall allow a continuous rotation in the clockwise and counterclockwise directions.  The mechanism shall operate freely.

- Torque Output Angle

  - The ERAD output drive axis shall be perpendicular to the input drive axis.

- Output-to-Input Rotation

  - The ERAD shall have an output drive rotational direction that is the same as the input drive rotational direction.

- Handle Lock

  - The ERAD handle shall be capable of being deployed and locked in eight (8) positions (in 45 degree increments) around the ERAD drive train.

- Handle Position

  - The ERAD handle shall be stowable, and shall have at minimum at least two (2) detent positions (0 degrees [fully stowed] and 90 degrees [fully deployed]).

- Reporting

The contractor shall provide weekly technical status, a bi-monthly schedule review, and monthly financial management reports as directed in the data requirements table.

- Earned Value

The contractor shall provide data pertaining to earned value reporting for the milestones identified in the “Interim Milestones” Table.

- Government Provided Equipment

See Government Furnished Property section.

- Project Management Plan

The contractor is not required to generate a Project Management Plan (PMP).

Deliverables/Products:

| Product | Description | Qty | Due | Class |
| --- | --- | --- | --- | --- |
| Hardware |  |  |  |  |
| Mock Up |  |  |  |  |
| Prototype | Functional Prototype for engineering testing | 1 | 5/1/07 | III |
| Certification | Full Class I Flight certification including thermal, load and vibration |  |  |  |
| Flight | Full acceptance testing | 5 |  | I |
| Training | N/A |  |  |  |
| Other | Qualification Unit | 1 |  | I/II |
| Test | Functional testing (acceptance and qualification) | N/A |  | I / qual |
| Software | N/A | N/A | N/A | N/A |
| Other Products | Acceptance Data Package (ADP) for each flight and qualification units | 1 per each flight / qual unit |  | I / II |
| Other Products | GCAR | 1 | 8/28/08 | N/A |

SCHEDULE

Start Date:  February 5, 2007			Finish Date:	July 25, 2008

| ITERIM MILESTONES | DUE DATES |
| --- | --- |
| System Requirements Review (SRR) | Suggested date 3/1/07 |
| Prototype Fabricated | Suggested date 5/1/07 |
| Prototype Testing Completed | Suggested date 6/1/07 |
| Preliminary Design Review (PDR) | Suggested date 6/15/07 |
| Critical Design Review (CDR) | Suggested date 10/16/07 |
| Hardware Fabrication Complete | Suggested date 2/15/08 |
| Hardware Qual / Acceptance Testing Complete | Suggested date 5/16/08 |
| Certification Complete | Suggested date 6/17/08 |
| SAR | Suggested date 7/1/08 |
| Hardware Delivery | 7/25/08 |
| Milestones, along with subjective measurements, are to be used for measuring performance. For schedule detail see Microsoft Project file located on the CRAVE web site for this DO listed under the Government Cost Estimate below. |

Government Estimate Located in RFQ File in Microsoft Project File On CRAVE Web Site

The file is titled:  EVA Electric CIPA gun.mpp

Total Government Estimate for this DO: $1200K

Option 1:  $___    (See Attachment 1)

Option 2:  $           (See Attachment 2)

TOTAL COST ESTIMATE FOR THIS DO:  $(Contractor Complete)

FEE:  $  (If Applicable)

OPTION 1:  $ N/A   (See Attachment 1)

OPTION 2: $  N/A   (See Attachment 2)

DATA REQUIREMENTS

Notes:  1.   Grey Scaled Rows Need No Additional/Required Fill-ins.

2.  On all other rows, If Necessary, Fill in Additional

Rqmts/Deliveries in last Column.

| DRD # | DATA TYPE | DRD TITLE | DUE | FREQUENCY | REQUIRED FOR DO? Y/N | COMMENTS |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Written Approval | Flight GFE Configuration Management Plan | With Proposal | Once | Attachment J-8 |  |
| 2 | Mandatory Submittal | Regular Status Report/ Summary Review | Thirty (30) days following contract start | Monthly | Y | Weekly Tech status |
| 3 | Written Approval | Project Technical Requirements Specification | If Required for DO See Comments | Once with Revisions | N |  |
| 4 | Mandatory Submittal if Flt H/W | GFE Systems Requirements Data Package | If Required for DO See Comments | Once with Revisions | N |  |
| 5 | Written Approval | Flight GFE Projects Requirements & Verification Document | If Required for DO See Comments | Once with Revisions | N |  |
| 6 | Mandatory Submittal if Flt H/W | Preliminary Design Review Data Package | If Required for DO See Comments | Once with Revisions | Y |  |
| 7 | Written Approval | Flight GFE Workmanship Specifications List | If Required for DO See Comments | Once with Revisions | Y |  |
| 8 | Written Approval | Project Schedule | PDR or 10% effort complete Milestone | Once w/Revisions (due w/DO proposal, updates & details provided as DO progresses) | Y |  |
| 9 | Written Approval | Flight GFE Interface Control Document | If Required for DO See Comments | Once with Revisions | Y |  |
| 10 | Written Approval | GFE End Item Specification | If Required for DO See Comments | Once with Revisions | N |  |
| 11 | Mandatory Submittal if Flt H/W | Flight GFE Failure Analysis Report | If Required for DO See Comments | As Required | Y |  |
| 12 | Written Approval | Flight GFE Verification and Validation Plan | As Specified in WI-EA-023 | Once with Revisions | Y |  |
| 13 | Written Approval | GFE Software Requirements Specification | If Required for DO See Comments | Once with Revisions | N |  |
| 14 | Written Approval | GFE Software Development Plan | If Required for DO See Comments | Once with Revisions | N |  |
| 15 | Written Approval | GFE Software Design Document | If Required for DO See Comments | As Required | N |  |
| 16 | Written Approval | Engineering Drawings | If Required for DO See Comments | Once with Revisions | Y | Pro-E format CAD Models and Drawing files |
| 17 | Written Approval | EEE Parts Lists and Analysis Report | If Required for DO See Comments | As Required | N | No EEE parts |
| 18 | Mandatory Submittal if Flt H/W | Critical Design Review Data Package | If Required for DO See Comments | Once with Revisions | Y |  |
| 19 | Mandatory Submittal if Flt H/W | Engineering Drawing Change Proposal | If Required for DO See Comments | As Required | Y |  |
| 20 | Written Approval | GFE Qualification Test Procedure | If Required for DO See Comments | Once with Revisions | Y |  |
| 21 | Written Approval | Flight Product User’s Guide | If Required for DO See Comments | Once with Revisions | N |  |
| 22 | Mandatory Submittal if Flt H/W | Software Code | If Required for DO See Comments | As Required | N |  |
| 23 | Written Approval | Information Technology (IT) Security Program Plan and Reports | (30) days after DO award, and as specified in JPG 2810.1 | JPG 2810.1 | Attachment J-4 Due 30 days after DO award |  |
| 24 | Written Approval | Certification Plan | If Required for DO See Comments | Once with Revisions | Y |  |
| 25 | Mandatory Submittal if Flt H/W | Certification Report | If Required for DO See Comments | Once with Revisions | Y |  |
| 26 | Mandatory Submittal if Flt H/W | Engineering Analysis | If Required for DO See Comments | As Required | Y |  |
| 27 | Mandatory Submittal if Flt H/W | Acceptance Data Package | If Required for DO See Comments | One Time | Y | Supplied for qual and Flight Units |
| 28 | Mandatory Submittal | Export Control Audit Results | After award of 1st DO, yearly on Sept. 30 thereafter | Yearly | Y |  |
| 29 | Written Approval | Quality Plan | With Proposal | Once with Revisions | Attachment J-11 | Only if contractor is using the R-quality plan template instead of ISO, and only if they need to make changes to it. |
| 30 | Written Approval | Patent Rights-Retention | As Required | As Required | Y (If Applicable) |  |
| 31 | Written Approval | Shuttle/Station Payload Safety Data Package | If Required for DO See Comments | As Required | N |  |
| 32 | Mandatory Submittal if Flt H/W | Limited Life Systems List | If Required for DO See Comments | As Required | Y |  |
| 33 | Written Approval | Space Station GFE Failure Modes and Effects Analysis and Critical Items List | If Required for DO See Comments | As Required | Y | If applicable |
| 34 | Written Approval | Space Shuttle GFE Safety and Analysis Report &Hazard Report | If Required for DO See Comments | As Required | N | If applicable |
| 35 | Written Approval | Software Quality Assurance Plan Report | 90 Days Prior to Software Development | Once with Revisions | N |  |
| 36 | Written Approval | ISS Hazard Report | If Required for DO See Comments | As Required | Y | If applicable |
| 37 | Upon Request | Reliability and Maintainability Plan | With Proposal | One Time | Y |  |
| 38 | Written Approval | Government Certification Approval Request (GCAR) | If Required for DO See Comments | As Required | Y |  |
| 39 | Written Approval | Risk Assessment Executive Summary Report (RAESR) | If Required for DO See Comments | As Required | Y |  |
| 40 | Written Approval | Problem Reporting and Corrective Action (PRACA) | 2 business days of problem isolation but no later than 10 days after detection | As Required | Y |  |
| 41 | Upon Request | Nonconformance Record | If Required for DO See Comments | As Required | Y |  |
| 42 | Mandatory Submittal | Government Industry Data Exchange Program and NASA Advisory Problem Data | Reported one time when discrepancy occurs | Once with Revisions | Y |  |
| 43 | Written Approval | Electrical, Electronic, and Electromechnical (EEE) Parts Control Plan | If Required for DO See Comments | Once with Revisions | N |  |
| 44 | Mandatory Submittal if Flt H/W | Certification Data Package | If Required for DO See Comments | Once with Revisions | Y |  |
| 45 | Written Approval | Certification and Acceptance Requirements Document | At CDR | Once with Revisions | Y |  |
| 46 | Upon Request | Wage/Salary and Fringe Benefit Data | Thirty (30) days after issuance of each DO | Once | N |  |
| 47 | Written Approval | GFE Acceptance Test Procedure | If Required for DO See Comments | One Time | Y |  |
| 48 | Mandatory Submittal if Flt H/W | Flight GFE Verification & Validation Report | If Required for DO See Comments | Once with Revisions | Y |  |
| 49 | Mandatory Submittal if Flt H/W | Space Shuttle GFE Failure Modes and Effects Analysis (FMEA) and Critical Items List | If Required for DO See Comments | As Required | Y | If applicable |
| 50 |  | Reserved | --- | --- | --- | --- |
| 51 | Mandatory Submittal | NASA Contractor Financial Management Reporting | After Issuance of 1st DO | Monthly | Y |  |
| 52 | Written Approval | Government Property Management Plan | With Proposal | Once with Revisions | Attachment J-7 |  |
| 53 | Mandatory Submittal | System Safety Plan | With Proposal | One Time | Attachment J-10 |  |
| 54 | Written Approval | R-Quality Plan Template | With Proposal/ Revisions as Required | Only applicable to B-CRAVE contracts in accordance with the SOW and the DRD | N |  |

Type 1 = Written Approval               Type 2 = Mandatory Submittal                Type 3 = Submittal Upon Request

GOVERNMENT FURNISHED PROPERTY  - The list of items below will be provided as Government Furnished Property.

| Item | Part Number | Quantity | Value |
| --- | --- | --- | --- |
| 3/8” Male Drive Go/No-Go Gage | SDG38114280-001 | 1 | $ 2000 each |
| DPT Go/No-Go Gage | SDG38114281-001 | 1 | $ 2000 each |
| McTether Load Fixture (Gage) | SDG38114296-001 | 1 | $ 3000 each |
| DPT PIP Pin Gage | SDG38114295-001 | 1 | $ 2000 each |
|  | (available by October 15, 2007) |  |  |