D-Zero Detector Central Fiber Tracker (CFT) Axial Project

Readout Electronics

Central Tracker Trigger (CTT) Mixer System

Date: April 1st, 2000

Revision Date: February 28th, 2003

N. George Wilcer, S. Marco Rapisarda

Document # ESE-D0-000401

Table of contents

1.	People and acknowledgements	7

2.	Introduction	8

Figure 2.1, picture of the mixer system subrack.	8

Figure 2.2, Data flow	10

3.	DAQ System Components	12

3.1	Front End Data Flow	14

Figure 3.1, Front End data flow.	14

3.2	Supersector and Mixer Board Data Flow	15

Figure 3.2, Supersector data flow.	16

Figure 3.3, Mixer Board data flow.	17

3.3	Data frame structure and timing	18

Figure 3.4, Master clock, data timing and frame structure at the output of the LVDS receivers	18

3.4	Mixer Board Block Diagram	19

Figure 3.5, Mixer Board Block Diagram	21

4.	Interfaces		22

4.1	LVDS Links Inputs from AFEs	22

Figure 4.1, LVDS Input links logic block.	22

Table 4.1, Signal assignments for the LVDS inputs connector.	23

4.2	LVDS Links Outputs to DFEs	24

Figure 4.2, LVDS Output links logic block.	24

Table 4.2, Signal assignments for the LVDS outputs connector.	25

4.3	LVDS Cabling	26

Figure 4.3, LVDS cabling.for a 28 bit wide link.	26

Figure 4.4, 28 bit link (3x5) LVDS cable.	26

4.4	Mixer System Backplane	27

Figure 4.5, Mixer System backplane	28

4.5	Mixer Board - Subrack Controller General Purpose Bus interface	29

Figure 4.6, Address bits.	29

Table 4.3, Mixer System Subrack slot addressing	29

4.5.1	Bus Signals	30

Figure 4.7, General Purpose Bus signals.	30

Table 4.4, General Purpose Bus signals.	30

4.5.2	Write and Read Cycles	31

Figure 4.8, Write operation timing	31

Figure 4.9, Read operation timing	32

4.5.3	Data Space Description	33

Table 4.5, Data space address map.	33

4.5.4	Board Status/Control register	34

Figure 4.10, Board Status/Control Register.	34

Table 4.6, Board Status/Control Register.	34

4.5.5	Device Status/Control register	35

Figure 4.11, Device Status/Control Register.	35

Table 4.7, Device Status/Control Register.	36

4.5.6	Device Configuration Data register	36

Figure 4.12, Device Configuration Data Register	36

4.5.7	Device Firmware ID register	36

Figure 4.13, Firmware ID Register.	36

Table 4.8, Device Firmware ID Register.	37

4.5.8	Mode of Operation register	37

Figure 4.14, Mode of Operation register	37

Table 4.9, Mode of Operation Register.	37

4.5.9	Input Links Error Status registers	38

Figure 4.15, Input Links Error Status Registers	38

Table 4.10, Input Links Error Status Low Register	38

Table 4.11, Input Links Error Status High Register	38

4.5.10	Device Access-Address register	39

Figure 4.16, Device Access-Address register	39

Table 4.12, Device Access-Address register.	39

4.5.11	Device Access-Data register	39

Figure 4.17, Device Access Data register	39

Table 4.13, Device Access register.	39

4.5.12	Device Access Structure	40

Figure 4.18, Device Access Structure	40

4.5.13	Output Links Test Mode registers	41

Figure 4.19, DFE0 and DFE1 Output Links Test Mode Registers	41

Table 4.14, DFE0 Output Links Test Mode Register	41

Table 4.15, DFE1 Output Links Test Mode Register	41

4.5.14	Monitoring Mode register	42

Figure 4.20, Monitoring Mode Register	42

Table 4.16, Monitoring Mode Register	42

4.5.15	Monitoring Status registers	43

Figure 4.21, Monitoring Status Registers	43

Table 4.17, Monitoring Status Low Register	43

Table 4.18, Monitoring Status High Register	43

4.5.16	Monitoring Status History registers	44

Figure 4.22, Monitoring Status History Registers	44

Table 4.19, Monitoring Status Low History Register	44

Table 4.20, Monitoring Status High History Register	44

4.5.17	Board Status/Control register B	45

Figure 4.23, Board Status/Control Register B.	45

Table 4.21, Board Status/Control Register B.	45

4.5.18	FIFO Trigger Control register	45

Figure 4.24, FIFO Trigger Control Register.	45

Table 4.22, FIFO Trigger Control Register.	46

4.5.19	Read/Write Test register	46

4.5.20	Firmware Revision Date registers	46

4.5.21	Board Serial Number register	46

4.6	Mixer Board - Subrack Controller Slow Monitoring Serial Bus interface	47

Figure 4.25, Slow Monitoring Bus signals	47

Figure 4.26, Slow Monitoring Bus register	47

Table 4.23, Slow Monitoring Bus Register	48

4.7	JTAG Interface	49

Figure 4.27, JTAG Connectors pinout	49

Table 4.24, JTAG Chain#1 Devices	49

Table 4.25, JTAG Chain#2 Devices	50

Table 4.26, Boundary Scan Description Language (BSDL) Files	50

4.8	Logic Analyzer Connectors	51

Table 4.27, HP Logic Analyzer connector J3 (suggested analyzer pods: 1 and 2)	51

Table 4.28, HP Logic Analyzer connector J5 (suggested analyzer pods: 3 and 4)	52

Table 4.29, HP Logic Analyzer connector J7 (suggested analyzer pods: 5 and 6)	53

Table 4.30, HP Logic Analyzer connector J7 preset configuration 0 (default, 21 bit link monitoring)	54

Table 4.31, HP Logic Analyzer connector J7 preset configuration 1 (28 bit link monitoring)	55

4.9	Power Supply and safety features	56

5.	Mixer Board Configuration	57

5.1	Configuration through JTAG	57

5.2	Configuration through the subrack general purpose bus.	58

Table 5.1, Configuration Files denomination.	58

Table 5.2, Mixer# and Subrack slot#.	58

6.	Monitoring and Debugging features	60

6.1	Front Panel LEDs	60

The front panel accommodates sixteen bicolor LEDs numbered from 0 to 15 and two red LEDs (see	60

Figure 6.1, Front panel LEDs and LEDs monitoring mode	60

Table 6.1, LED's set #0 (input links clock and DLLs status).	61

Table 6.2, LED's set #1 (input links SYNC bit status).	61

Table 6.2, LED's set #2 (input links Walking 1 test pattern detection).	61

Table 6.3, LED's set #3 (input links Walking 0 test pattern detection).	61

Table 6.2, LED's set #4 (input links SYNC bit status after synchronization).	61

Table 6.4, LED's set #5 (input links frame synchronization status).	61

Table 6.5, LED's set #6 (Output links test pattern detection).	62

Table 6.6, LED's set #7 (Input links control bits stream monitoring).	62

Table 6.7, LED's set #8 (Mixer Board local bus monitoring).	62

Table 6.8, LED's set #9 (Backplane serial bus and A16:D8 bus control signals monitoring).	63

Table 6.5, LED's set #10 (Backplane A16:D8 general purpose bus address signals monitoring).	63

Table 6.5, LED's set #11 (A16:D8 general purpose bus data and slot address signals monitoring).	64

Table 6.6, LED's set #12 (Default mode, FPGA configuration status).	64

Table 6.7, LED's set #13 (Output Links Test Mode Enable status).	65

Table 6.7, LED's set #14 .(Input Links Error Status).	65

Table 6.7, LED's set #15 (LED Test).	65

7.	Appendix A – Devices registers	66

7.1	FrontEnd Devices	66

Table 7.1, Front-End devices registers.	67

7.1.1	Device Firmware Register	68

Figure 7.1, Device Firmware register.	68

7.1.2	Link pointer register	68

Figure 7.2, Link Pointer register	68

7.1.3	Input Link Status registers	69

Figure 7.3, Input Link Status register.	69

7.1.4	Input Link Control register	69

Figure 7.4, Input Link Control register	69

Figure 7.5, Data synchronization and link controls.	69

7.1.5	Frame Sync Status register	70

Figure 7.6, Frame Synchronization Status register.	70

Figure 7.7, Frame Synchronization Status register content.	70

7.1.6	Frame Sync Status History register	71

Figure 7.8, Frame Synchronization Status History register.	71

7.1.7	Input Link Control Bits Mask register	71

Figure 7.9, Input Link Control Bits Mask register.	71

7.1.8	Input Link Control Bits Status registers	72

Figure 7.10, Input Link Control Bits Status register	72

7.1.9	Input Link Control Bits Status at Link#0 FPGA register	72

Figure 7.11, Input Link Control Bits Status register	72

7.1.10	Embedded Command Bits status register	73

Figure 7.12, Embedded Command Bits Status Register.	73

7.1.11	Embedded Command Status Bits status register	73

Figure 7.13, Embedded Command Status Bits Status Register.	73

7.1.12	Monitoring Mode 7 Mask register	74

Figure 7.14, Monitoring Mode 7 Mask register.	74

7.2	Backplane Devices	75

Table 7.2, Backplane Devices registers.	75

7.2.1	Device Firmware Register	76

7.2.2	Device Control register	76

Figure 7.15, Device Control register	76

7.2.3	Clock DLL Error register	76

Figure 7.16, Clock DLL Error register.	76

7.2.4	Clock Frequency Error register	76

Figure 7.17, Clock Frequency Error register.	76

7.2.5	SYNC Error register	77

Figure 7.18, SYNC Error register	77

7.2.6	Clock/SYNC Select Status register	77

Figure 7.19, Clock/SYNC Select Status register	77

7.2.7	Backplane Driver Status register	78

7.2.8	Backplane Driver Control register	78

7.2.9	Backplane Receiver Status register	78

7.2.10	Backplane Receiver Control register	78

7.3	BackEnd Devices	79

Table 7.3, BackEnd Devices registers.	79

7.3.1	Device Firmware Register	79

7.3.2	Device Control Register	79

7.3.3	Output Link Status register	80

7.3.4	Output Link Control register	80

Figure 7.20, Link Control register	80

7.3.5	Output Link Embedded Command Bits Mask register	80

Figure 7.21, Embedded Command Bits Mask register.	80

7.3.6	Output Link FIFO	81

Figure 7.22, Output Link FIFO	81

Figure 7.23, Output Link FIFO Access/Control Structure	81

7.3.7	Output Link FIFO Memory Pointer register	82

Figure 7.24, Output Link FIFO Memory Pointer register	82

7.3.8	Output Link FIFO Control register	83

Figure 7.25, Output Link FIFO Control register	83

Table 7.4, Output Link FIFO Control Register.	83

7.3.9	Output Link FIFO Data Access register	83

Figure 7.26, Output Link FIFO Data Access register	83

8.	Appendix B – Mixer Board detailed block diagrams	84

8.1	Mixer Board data flow from LVDS receivers to LVDS transmitters	84

Figure 8.1, Mixer Board simplified data flow	85

8.2	Mixer Board Front-End FPGAs	86

Figure 8.2, Mixer Board Front-End FPGAs	86

8.3	Mixer Board Back End FPGAs	87

Figure 8.3, Mixer Board Back-End FPGAs	87

8.4	Mixer Board Backplane FPGAs	88

Figure 8.4, Mixer Board Backplane FPGAs	88

8.5	Control bits (inputs) and command bits (outputs)	89

Figure 8.5, Command bits generation, timing and denomination.	89

8.6	Mixer Board Board-Controller	90

Figure 8.6, Mixer Board Controller	90

8.7	Mixer System Timing Signals Distribution	91

Figure 8.7, Mixer Master clock selection	91

Figure 8.8, Mixer Slave clock selection	91

Figure 8.9, Mixer System Clock Distribution	93

8.8	Mixer System Data Synchronization	94

Figure 8.10, Mixer System Data Synchronization	94

8.9	Mixer Board Frame Synchronization	95

Figure 8.11, Mixer Board Frame Synchronization signals	95

8.10	Mixer Board spare connections	96

Figure 8.12, Mixer Board spare connections	96

Table 8.1, Spare connections usage.	98

9.	Appendix C - Mixer Board Printed Circuit Board Interconnection Matrix	99

Figure 9.1, Link #0 (CPS) Interconnection Matrix.	99

Figure 9.2, Link #1 Interconnection Matrix	100

Figure 9.3, Link #2 Interconnection Matrix	100

Figure 9.4, Link #3 Interconnection Matrix	101

Figure 9.5, Link #4 Interconnection Matrix	101

Figure 9.6, Link #5 Interconnection Matrix	102

Figure 9.7, Link #6 Interconnection Matrix	102

Figure 9.8, Link #7 Interconnection Matrix	103

Figure 9.9, Link #8 Interconnection Matrix	103

Figure 9.10, Link #9 Interconnection Matrix	104

Figure 9.11, Link #10 Interconnection Matrix	104

Figure 9.12, Link #11 Interconnection Matrix	105

Figure 9.13, Link #12 Interconnection Matrix	105

Figure 9.14, Link #13 Interconnection Matrix	106

Figure 9.15, Link #14 Interconnection Matrix	106

Figure 9.16, Link #15 Interconnection Matrix	107

Figure 9.17, Backplane DFE0 Receiver Interconnection Matrix.	108

Figure 9.18, Backplane DFE1 Receiver Interconnection Matrix.	109

10.	Appendix D - Mixer System Backplane connectors pinout	110

Table 10.1, Pin/Signal assignments for the backplane top section connector	110

Table 10.2, Pin/Signal assignments for the backplane bottom section connector.	111

11.	Appendix E - Test Patterns specification	112

11.1	Input links test patterns	112

Table 11.1, Input Links walking 1 test pattern.	113

11.2	Output links test patterns	114

Table 11.2, Output Links test patterns.	114

Table 11.3, Link relative sector and color encoding in the output links test pattern.	115

12.	Appendix F – Mixer Board Components and Layout	116

Table 12.1, Mixer Board component list.	117

Table 12.2, Printed Circuit Board stacking.	118

Figure 12.1, Mixer Board.	119

13.	Appendix G – Input and Output Links cabling	120

13.1	Mixer System Input Links cabling map	120

Table 13.1, Slot#2 and Slot#3 (Supersector#4).	120

Table 13.2, Slot#4 and Slot#5 (Supersector#4).	120

Table 13.3, Slot#6 and Slot#7 (Supersector#5).	121

Table 13.4, Slot#8 and Slot#9 (Supersector#5).	121

Table 13.5, Slot#10 and Slot#11 (Supersector#1).	122

Table 13.6, Slot#12 and Slot#13 (Supersector#1).	122

Table 13.7, Slot#14 and Slot#15 (Supersector#2).	123

Table 13.8, Slot#16 and Slot#17 (Supersector#2).	123

Table 13.9, Slot#18 and Slot#19 (Supersector#3).	124

Table 13.10, Slot#20 and Slot#21 (Supersector#3).	124

13.2	Mixer System Input Links cabling map organized by cassette	125

Table 13.11, AFE Cassettes 26 (CPS) and 28 (CPS).	125

Table 13.12, AFE Cassettes 29 and 30.	125

Table 13.13, AFE Cassettes 31 and 32	125

Table 13.14, AFE Cassettes 33 and 34	126

Table 13.15, AFE Cassettes 35 and 36	126

Table 13.16, AFE Cassettes 37 and 38	126

Table 13.17, AFE Cassettes 39 and 40	127

Table 13.18, AFE Cassettes 41 and 42	127

Table 13.19, AFE Cassettes 43 and 44	127

Table 13.20, AFE Cassettes 45 and 46	128

Table 13.21, AFE Cassettes 47 and 48	128

Table 13.22, AFE Cassettes 49 and 50	128

Table 13.23, AFE Cassettes 51 and 52	129

Table 13.24, AFE Cassettes 53 and 54	129

Table 13.25, AFE Cassettes 55 and 56	129

Table 13.26, AFE Cassettes 57 and 58	130

Table 13.27, AFE Cassettes 59 and 60	130

Table 13.28, AFE Cassettes 61 and 62	130

Table 13.29, AFE Cassettes 63 and 64	131

Table 13.30, AFE Cassettes 65 and 66	131

Table 13.31, AFE Cassettes 68 (CPS) and 70 (CPS).	131

Table 13.32, AFE Cassette 72 (CPS).	132

Table 13.33, Relative and Absolute Cassette numbers.	132

13.3	Mixer System Output Links cabling map	133

Table 13.34, Mixer Board output links and DFE input links arrangements on the front panels.	133

Table 13.35, Slot#2 and Slot#3 (Supersector#4).	134

Table 13.36, Slot#4 and Slot#5 (Supersector#4).	134

Table 13.37, Slot#6 and Slot#7 (Supersector#5).	135

Table 13.38, Slot#8 and Slot#9 (Supersector#5).	135

Table 13.39, Slot#10 and Slot#11 (Supersector#1).	136

Table 13.40, Slot#12 and Slot#13 (Supersector#1).	136

Table 13.41, Slot#14 and Slot#15 (Supersector#2).	137

Table 13.42, Slot#16 and Slot#17 (Supersector#2).	137

Table 13.43, Slot#18 and Slot#19 (Supersector#3).	138

Table 13.44, Slot#20 and Slot#21 (Supersector#3).	138

14.	Appendix H – Subrack Controller	139

14.1	Subrack Controller	139

Figure 14.1, Subrack controller simplified block diagram	140

Figure 14.2, Subrack Controller (DFEC) Status Word.	140

14.2	CompactFlash™ card	141

Figure 14.3, CompactFlash card.	141

14.2.1	General information about Compact Flash cards [Ref. 15]	141

14.2.2	Standard subrack controller commands (autoexec) files	141

Table 14.1, content of file "autoexec.000".	143

Table 14.2, content of file "autoexec.001".	144

14.3	Subrack Controller Commands	145

14.3.1	Examples of command usage	146

Table 14.3, Example of mixer board reset operation.	146

Table 14.4, Example of change LED monitoring mode operation.	146

Table 14.5, Example of device access operations.	146

14.4	Test procedures information	147

14.5	Diagnostic procedures information	147

15.	Appendix I – CPS re-mapping conversion tables	148

Table 15.1, Mixer 1 CPS data bits re-mapping.	148

Table 15.2, Mixer 2 CPS data bits re-mapping.	149

Table 15.3, Mixer 3 CPS data bits re-mapping.	150

Table 15.4, Mixer 4 CPS data bits re-mapping.	151

16.	Appendix L - Notes about Input Links swapping	152

Table 16.1, Link swapping information.	152

17.	Glossary		153

Figure 17.1, Switching standards.	156

Figure 17.2, Comparison of switching standards.	156

18.	References		158

# People and acknowledgements

S. Marco Rapisarda, responsibilities: project leader, system design, VHDL firmware, system commissioning, and system documentation.
E-mail: rapisard@fnal.gov
Phone: (630) 840-6559.

N. George Wilcer, responsibilities: electrical schematics, printed circuit board layouts, test software, system testing and quality control. 
E-mail: wilcer@fnal.gov
Phone: (630) 840-2749.

Major and fundamental contributions to the design of the mixer system came from the following people:

John Anderson [Ref. 7], Bob Angstadt [Ref. 6], Fred Borcherding [Ref. 4], Bill Haynes, Don Husby, Jamieson Olsen [Ref. 5], John Smith, Mario Vaz.

Invaluable help to the assembly, debugging and commissioning of the mixer system came from the following people:

Stewart Bledsoe, John Chramowicz, Stefan Gruenendahl, George Ginther, Stephen Lynn, Paul Rubinov, Makoto Tomoto [Ref. 8b].

# Introduction

This document describes the mixer system, part of the readout electronics of the D-Zero detector Central Fiber Tracker (CFT) at Fermilab. More information on the experiments performed at Fermilab is available on the laboratory web page: http://www.fnal.gov/

More information on the D0 Detector is available on: http://www-d0.fnal.gov/

The designers welcome suggestions and corrections [Ref. 41], which can be addressed directly to the engineer responsible of the project. Contact information is available on the Electronics System Engineering Department (ESE) web page: http://www-ese.fnal.gov/

More information and documentation on the Mixer Project are available on:

http://www-ese.fnal.gov/D0_CTT_MIXER/

Figure 2.1, picture of the mixer system subrack.

A custom digital data Mixer System has been designed to reorganize, in real time, the data produced by the Fermilab D0 Scintillating Fiber Detector. The data is used for the level 1 trigger generation. The Mixer System receives the data from the front-end digitization electronics over 320 Low Voltage Differential Signaling (LVDS) links running at 371 MHz. The input data is de-serialized down to 53 MHz by the LVDS receivers, clock/frame re-synchronized and multiplexed in Field Programmable Gate Arrays (FPGAs). The data is then re-serialized at 371 MHz by LVDS transmitters over 320 LVDS output links and sent to the electronics responsible for level 1 trigger decisions. The Mixer System processes 311 Gigabits per second of data with an input to output delay of 200 nanoseconds.

To find a conceptual design solution that would comply with the design specification a software tool was designed and implemented. The tool allowed us to graphically visualize and analyze the data information and investigate possible design architectures. The tool was also used to generate the portion of VHDL code defining data multiplexing.

The Mixer System diagnostics allow monitoring input links, clock frequency, frame markers, control bits, clock synchronization, frame realignment and detecting/sending test patterns. The input links test pattern recognition and output links test pattern transmission is used by the trigger system diagnostic to verify the integrity and correctness of the cabling. The Mixer System diagnostic is remotely accessible. A simplified version of the diagnostic using bi-color LEDs on the Mixer board's front panel allow the user to view in real-time the status of signals and flags.

A component of the D0 Detector at Fermilab is the Central Fiber Tracker (CFT). The CFT is constructed of scintillating fibers that are organized together in a very precise array of ribbons, placed onto a structure formed by eight co-axial cylinders. The energy deposited into the scintillating fibers by particle interactions is transformed into visible light. The light travels through the scintillating fiber and through an optical (clear) fiber connected to it, reaching a very sensitive light detector, the Visible Light Photon Counter (VLPC), hosted in a liquid helium cryostat. The VLPCs are a derivative of solid-state photomultipliers and are used to convert the scintillation light into electrical signals. These are discriminated and digitized by the Analog Front-End boards (AFEs). The Mixer System receives the digitized data from the AFEs, then processes and re-organizes it in real-time with minimal delay from cylindrical geometry into 80 azimuthal wedges or sectors. The restructured data are transmitted to the Digital Front End (DFE) board system. The DFE system uses the data to contribute to level 1 and level 2 trigger decisions.

Because the Mixer System was specified as a late addition to a previously designed system, there were many design constraints forced on the system. The most challenging constraints were the limited space available, the restricted access location, the system timing requiring minimal input to output delay, the number of input/output links, the clock/frame resynchronization of the input links data streams. A particular demanding constraint was the already fixed throughput of the Mixer System I/O links, just barely sufficient for the detector's data throughput. Due to limited budget and time available for the project, the specification also called for a custom design with minimal flexibility. Furthermore, the possible flavors of the Mixer board had to be based on the same hardware, so that only one board design would be needed. The fact that the system was to be installed in a limited access area also suggested a need for the capability to remotely run diagnostics and remotely update the system firmware.

Figure 2.2, Data flow

The Mixer System consists of a 21-slot 6U subrack with a custom backplane. The subrack type was an initial constraint resulting from limited rack space available for a new component of the trigger system. The Mixer subrack first slot hosts a custom subrack controller, and the remaining slots host twenty Mixer boards. These twenty Mixer boards can be logically partitioned in five subsystems of four boards. This partitioning matches the fiber detector partitioning in five 72° wide sections or supersectors. This mechanical symmetry allows each supersector to be considered identical from the Mixer System's point of view. Each Mixer subsystem exclusively handles the data of one supersector, and because of detector symmetry, all five subsystems can use the same firmware. A portion of the data received by each of the Mixer boards, needs to be routed to another board in order to be part of the output data stream to which it belongs. The input links to the Mixer System have been arranged in such a way as to limit each Mixer board's data exchange to only the two adjacent boards. Furthermore, the five Mixer subsystems can be considered independent, because no data exchange is needed between them.

The Mixer System receives the data from the Analog Front-End boards over 320 Low Voltage Differential Signaling (LVDS) serializer/deserializer (SERDES) links, running at 371 MHz. The input links are of two types. 300 are 21 bits wide and 20 are 28 bits wide. The input data is de-serialized down to 53 MHz by the LVDS receivers, clock/frame re-synchronized and multiplexed in Field Programmable Gate Arrays (FPGAs), and then re-serialized at 371 MHz by the LVDS transmitters. The system has 320 LVDS SERDES output links, all are running at 371 MHz and all are 28 bits wide. Of the 320 output links only 240 carry unique data. The remaining 80 links have replicated data, and are needed to transmit some of the data to more than one DFE system's module. The Mixer System processes 311 Gigabits per second of data, with an input to output delay of 200 nanoseconds. Of this, 48 nanoseconds are used for data de-serialization/serialization, and 152 nanoseconds are used for data synchronization and mixing.

To find a conceptual design solution that would comply with the design specification, a software tool was designed and implemented. The tool is based on Microsoft Excel™ software package and makes extensive use of routines written in Visual Basic™ for Applications (VBA). The tool allows graphical visualization and analysis of the data. It also permits arranging of the data in order to minimize the required number of interconnections between inner elements of the Mixer System to reorganize the data into azimuthal trigger sectors. The tool was also used to decide between possible hardware architectures, and after the architecture was chosen, to generate the portion of VHDL code defining how the system's FPGAs should "mix" data.

The Mixer board uses a total of 17 FPGAs. One FPGA is used as the board controller and is programmed at power-up by an on-board EEPROM. It implements the interface with the custom subrack controller, providing access to board's controls, diagnostics and a means to configure the remaining 16 FPGAs. The FPGA configuration files are stored on a CompactFlash™ memory card hosted by the subrack controller. The system firmware can be updated by replacing the memory card, or when the system in not accessible, downloading the configuration files to the memory card using the subrack controller MIL-STD-1553 interface. Of the 16 remaining FPGAs, 6 are used as the board front-end to perform data clock synchronization and frame realignment, 4 are used to exchange data through the backplane, and 6 as the board back-end to perform the data mixing and drive the output link transmitters. One of the 4 backplane FPGAs is also used as clock controller, and handles the board's clock and frame timing signals. One of the four Mixer boards in each subsystem acts as a timing master, and propagates clock and frame marker signals through the subsystem, allowing synchronous operations.

One critical component of a Mixer board is the diagnostic firmware. It allows monitoring input links, clock frequency, frame markers, control bits, clock synchronization, frame alignment and detecting/sending test patterns. The input links test pattern recognition and output links test pattern transmission is used by the trigger system diagnostic to verify the integrity and correctness of the cabling. The Mixer diagnostic is remotely accessible through the MIL-STD-1553 system interface. A simplified version of the diagnostic uses the reset push-button and 16 bi-color LEDs on the Mixer board front panel. This allows the user to view, in real-time, the status of 256 signals and flags, by scrolling through 16 "monitoring modes". The front panel accessible diagnostic has proven to be extremely useful during system testing and installation.

The Mixer System was comprehensively exercised before the commissioning phase using a test system which, aside from a limited data throughput, emulates closely the real data environment.

The system commissioning phase ended in February of 2002, support for system integration is ongoing at D0, and at this time only minor firmware changes are foreseen.

# DAQ System Components

Scintillating Fiber Detector

Scintillating fibers are organized together in a very precise array of ribbons, placed onto a structure formed by eight co-axial cylinders (or layers). When a particle passes through a scintillating fiber, a brief flash of light occurs. The light travels through the scintillating fiber and through an optical (clear) fiber connected to it, reaching a very sensible light detector, a Visible Light Photon Counter (VLPC). The light generated in each of the 40960 detector's scintillating fibers goes to an independent VLPC.

Visible Light Photon Counters (VLPCs)

The VLPCs are a derivative of solid-state photomultipliers (SSPM) but different than their predecessor in that they are blind in the infrared region. VLPCs are solid-state detectors capable of detecting single photons having wavelength of 0.4 to 28 um. Their operational temperature is between 6 and 14 K, requiring a cryogenic environment to operate. They are used in the CTT system to convert the scintillation light into an electrical signal, which is discriminated and digitized by the Analog Front-End boards (AFEs).

Analog Front-End Boards (AFEs) [Ref. 7]

The AFEs, process the analog signals from the VLPC channels, and supply the generated data to the mixer system. Originally the Central Fiber Tracker system was supposed to have two flavors of Analog Front-End (AFE) boards, one with 8 Multichip Modules (MCMs) to read the axial fiber and a 12 MCMs board flavor to readout the preshower fibers. Due to technical issues the final system uses only 8 MCMs boards. The mixer system design started with the assumption of a CTT system having two types of AFEs and even if this is no more the case, that assumption affected design decisions and is the reason for choices that may not look clear in today's light. Being that the mixer system design was already completed at the time the decision to use only 8MCM AFEs was made, this document will still reflect in several parts the original assumption of two types of AFE boards.

The digital data generated by the analog front-end will be used by the logic responsible for the level 1 trigger decisions. But before the data can be used for trigger generation it needs to be reorganized into trigger sectors, this is done by the mixer system.

Mixer system  [Ref. 8]

The mixer system was conceived well after all the other CTT system components. The reasons for its existence are:

- The need for the logic generating the level 1 trigger (Digital Front-End boards) to receive the data organized in "trigger sectors".

- The difficulties arise in reorganizing the optical fiber in "trigger sectors" before the VLPCs. The mechanical design of the detector did not allow for the fiber ribbons to be arranged as desired/needed and the best option was the reorganization of the data after the digitizing process (AFEs).

Being the mixer system part of the electronics handling data used to generate a trigger, the data must be processed (re-organized) in real-time and with the minimum possible delay. The mixer system consists of a 21 slot 6U VME type subrack with custom backplane. Slot 1 is occupied by a custom subrack controller, slot 2 to slot 21 hosts twenty mixer boards.

Digital Front-End Boards (DFEs) [Ref. 5]

The "trigger sector organized" data produced by the mixer system is passed to the Digital Front End boards (DFEs) system that does the triggering. Following the Digital Front End, there is other electronics that concentrate the information, look for trigger information and send/broadcast it up to the framework (collectors and broadcasters).

## Front End Data Flow

Figure 3.1 shows the D0 Central Fiber Tracker (CTT) structure organized in angular sectors and trigger sectors.

Figure 3.1, Front End data flow.

The fiber detector can be partitioned in five 72° wide "supersectors". Each supersector can be partitioned into forty 9° wide "sector pairs" or eighty 4.5° wide "sectors". Each sector pair is split in six "trigger sectors" identified by a color (blue ●, red ●, yellow ●, orange ●, green ●, purple ●).

The trigger sectors represent the data grouping done by the mixer system before the data is sent to the Digital Front-End boards system for trigger generation.

The Analog Front-End board block diagram in Figure 3.1 still shows the two types of AFE boards originally planned for the CTT system. In the current system only the type labeled "CFT Analog Front-End board" is used.

## Supersector and Mixer Board Data Flow

From the mixer system point of view, the five supersectors look exactly the same. This is the reason for having the mixer system partitioned in five subsystems of four boards each. Every mixer subsystem handles the data from one supersector. Each of the five supersectors can be considered independent because no data exchange is needed between mixer subsystems.

This partitioning allowed concentrating the mixer system design effort on just a fifth of the detector and then replicating the subsystem for the other four supersectors.

Each Mixer board handles the data generated by two sector pairs. Because the data belonging to a particular set of two sector pairs is not necessarily received by the mixer board handling those sector pairs, there is the need of a board to board data exchange inside a mixer subsystem (four mixer boards). Thanks to the front-end system design, a mixer board needs to exchange data only with adjacent boards belonging to the same mixer subsystem.

The data from the Analog Front-End board system is received on Low Voltage Differential Signaling (LVDS) links. Two types of LVDS links are used, 21 bit wide to transmit CFT data and the 28 bit wide for CPS data. The data clock is, as it is for several systems at Fermilab, the Tevatron clock, which has a frequency of approximately 53 MHz. The LVDS transmitters on the AFEs serialize the data over balanced-pair conductors transmitting it with a clock seven times faster than the data clock (53MHz x 7= 371MHz). The LVDS receivers on the Mixer boards de-serialize the data received on the balanced pairs from 371 MHz LVDS back to 53 MHz Low Voltage TTL (LVTTL).

In a mixer subsystem (4 mixer boards) the data is reorganized and serialized again by LVDS transmitters and sent to the Digital Front-End boards system that is responsible for trigger generation. Aside from LVDS components, the mixer board operates in LVTTL. The board-to-board data exchange is also performed in LVTTL.

Each Mixer board has sixteen LVDS receivers; fifteen of them are the 21 bit wide type (CFT data, input link# 1 to 15) and one is the 28 bit wide type (CPS data, input link#0). There are also sixteen LVDS transmitters, all of them are the 28 bit wide type, and are used to send the reorganized data to the DFEs. The output links are divided into two groups. This division is reflected in the numbering scheme, the first group has link numbers from 00 to 07, the second group link# 10 to 17. Throughout the mixer project documentation the two groups of output links are referred to as DFE0 and DFE1 links (because most of them go to two different DFE boards), plain color links and striped color links (to avoid confusion between links having the same trigger sector color and belonging to different groups).

The DFE boards need to share some of the data sent by the mixer system. This is achieved by duplicating some of the output links. In each of the two groups of 8 output links of a mixer board six links are unique and two of the links (green and red) are duplicates.

Figure 3.2, Supersector data flow.

Figure 3.3, Mixer Board data flow.

## Data frame structure and timing

The data of a specific particle interaction event (or bunch crossing) is received and sent by the Mixer System over seven 53MHz clock cycles or seven "time slots", this group of seven time slots defines a "data frame". In order to separate data from different bunch crossings a frame synchronization signal is needed.

The Analog Front-End board (AFE) has a signal derived from the 7.6 MHz bunch crossing clock called LD_SHFT. The equivalent signal on the Mixer System is called SYNC. The AFE sends this signal to the Mixer System on the Least Significative bit (LSb) of each LVDS link.

The Mixer System is expecting the SYNC signal to be high in the last time slot of each frame. Figure 3.4 shows the default frame structure at the output of the Mixer board LVDS receivers.

Figure 3.4, Master clock, data timing and frame structure at the output of the LVDS receivers

The correct SYNC timing is critical to the functioning of the mixer system. The position of the SYNC bit lets the mixer logic know at each clock tick (or time slot) which data bits are being received and how they should be reorganized to generate the output links data stream.

The SYNC bit is regenerated by each mixer board and used as a frame marker for the output data stream sent by the Mixer System to the Digital Front-End boards. The SYNC bit for the input LVDS links from the AFEs and the output LVDS links to the DFEs is located on the least significative bit and is high in the last time slot of a data frame.

## Mixer Board Block Diagram

The mixer board can be logically partitioned in several logic blocks (see Figure 3.5):

- LVDS receivers. 
There are sixteen LVDS SERDES (serializer/deserializer) receivers on a mixer board. Fifteen receivers (link#1 to 15) are of the 21 bit wide type; they use the Texas Instrument SN65LVDS96 chip. One of the receiver (link#0) is of the 28 bit wide type and use the SN65LVDS94 chip. The output and the synthesized clock of the LVDS receivers is send to the Front-End FPGAs.

b)	Front-End FPGAs.
There are six Xilinx Virtex 50 series FPGAs used to receive the data and clocks from the input links. Five FPGAs handle the data of three links each, one FPGA handle only the data of link#0. The FPGAs logic performs diagnostic functions like clock and frame synchronization (SYNC bit) detection, but its main purpose is the input links data synchronization to a "global clock". After the data is synchronized it is sent to the Back-End FPGAs and the Backplane FPGAs that perform the data reorganization in "trigger sectors". The Front-End FPGA handling the data from link#0 also perform the function of collecting the control bits from all input links and using them to generate the two "Embedded Command Bits" which are forwarded to four Back-End FPGA and inserted in some of the output links data streams.

- Interconnection Matrix.
The interconnection matrix is made by all the connections used to forward the data from the Front-End FPGAs to the Back-End and Backplane FPGAs. The interconnection matrix is hardwired in the mixer printed circuit board and cannot be changed. The mixer board can be considered a custom digital data switch. The custom design allowed the designer to minimize the number of interconnections, fit the design in tight mechanical constraints, and to use quad flat packages for the FPGAs. One level of design complexity was added because of the requirement of having a unique mixer board design that fitted four different firmware versions, one for each of the four boards (mixer subsystem) handling the data from a supersector. The unpleasant side of a custom design is the very limited flexibility and this is particularly true for the mixer system. Minimal changes in the system specification may demand a different interconnection matrix that will require redesigning the printed circuit board.

- Backplane FPGAs.
Four Xilinx Virtex 50 series FPGAs are used to handle the data exchange with the adjacent mixer boards inside a mixers subsystem. Two FPGAs are used as "backplane drivers", one to send data to the board to the right and one for the board to the left. The two other FPGAs are used as "backplane receivers". Both receive the same data and each of them handle the data for a different "sector pair". This mean that each of the backplane receivers forward the received data to only three of the six Back-End FPGAs.

- Back-End FPGAs.
There are six Xilinx Spartan 40XL series FPGAs used to reorganize the data before sending it to the output link’s LDVS transmitters. They can be divided in two subsets of three FPGAs, each of them handling the data belonging to a different sector pair. These two subsets of chips will be often referred as DFE0 and DFE1 FPGAs or plain color FPGAs and striped color FPGAs. The four backplane FPGAs receive two Embedded Command Bits from the link#0 Front-End FPGA. These bits are inserted in some of the output data streams.

- LVDS transmitters.
There are sixteen LVDS SERDES (serializer/deserializer) transmitters on a mixer board. All of them are of the 28 bit wide type and are the Texas Instrument SN65LVDS93. The data inputs of the LVDS transmitters are driven by the Back-End FPGAs. As for the Front-End FPGAs the transmitters can be divided in two subsets referred to as DFE0 (or plain color) and DFE1 (or striped color). The DFE0 transmitters and links are numbered from 00 to 07, the DFE1 ones are numbered from 10 to 17. The color naming of the transmitters and links refer to the color assigned to the "trigger sector" in a "sector pair". Each transmitter/link handle the data belonging to one trigger sector. The DFE boards need to share some of the data sent by the mixer system. This is achieved with the duplication of some of the output links. In each of the two subsets of 8 output links of a mixer board six links are unique and two of the links (green and red) are duplicates.

- Control logic. One of the seventeen FPGAs on a mixer board is used as "board controller" and is automatically configured at power-up by an on board EEPROM. The board controller performs several functions:

  - Handles backplane communication with the subrack controller (slot 1 of the subrack). Read/Write operations are supported on a data space of several 8 bit-wide "registers". The board controller manages the configuration data download (from the subrack controller) to the other sixteen FPGAs.

  - Acts as central point of collection of information on board status and control of board behavior.

  - Relays FPGAs communications from/to the subrack controller.

An important block of the control logic is the "clock controller". Unlike the board controller it is not an individual FPGA. It is instead hosted by one of the backplane FPGAs, the backplane right driver. The clock controller supervises the distribution of the frame synchronization signal (SYNC) and clock on the mixer board. In particular it decides which clock the mixer board should use as "global clock" and which frame synchronization signal should be used as "global SYNC".

The leftmost board in a mixer subsystem (four boards handling the data from a supersector) is used as clock/SYNC "master" board; it distributes the clock/SYNC signals to the other three ("slave") boards in the subsystem. This allows for clock and frame synchronized operations and data exchange inside a mixer subsystem. The clock controller has the capability to detect the presence of the link#0 clock and the backplane clock. The local clock (53MHz on-board oscillator) is always available. The clock controller on a slave board will use the backplane clock as first choice, the link#0 clock as second choice and the local clock as third. The clock controller on a master board has only the last two options.

Figure 3.5, Mixer Board Block Diagram

# Interfaces

## LVDS Links Inputs from AFEs

The Mixer Board receives the data from the AFEs on two types of LVDS Links, 21 bits wide for the CFT fiber data and 28 bits wide for the CPS fiber data. On the 21 bit links the data is transmitted along four differential pair (three data and one clock), and on the 28 bit links the data is transmitted on five differential pair (four data and one clock). The Analog Front-End board uses the Texas Instrument serializers [Ref. 38] SN65LVDS95 and the SN65LVDS93 as transmitters and the Mixer Board uses the deserializers SN65LVDS96 and SN65LVDS94 as receivers which provide the 21 and 28 bits outputs of 3.3 V TTL data and clock.

The high-speed LVDS links interfacing the Analog Front End Boards with the Mixer System use 100 ( controlled-impedance custom parallel cables. The front panel connectors are the AMP 1-1064-1 [Ref. 13] which have a 50 ( single ended (signal to ground) and an 89 ( differential (signal to signal) impedance.

Special care was taken on the Mixer Board design to ensure that the highest signal integrity was maintained. To achieve this, the board's impedance was controlled to 50 ( single ended and 100 ( differential for the high-speed LVDS serial connections. The board's impedance was controlled to 50 ( for the slower parallel data. The quantity of vias was minimized and, when necessary, placed as close as possible to the device drivers. Since this is a combined serial and parallel interface, care was taken to control both impedance and trace length mismatch (board skew) [Ref. 38]. All traces from the connector to the receivers are as short as possible and matched in length. The 100 ( LVDS interconnecting media is matched with a 100 ( termination at the inputs of the receivers.

Figure 4.1, LVDS Input links logic block.

Table 4.1 shows the pinout of the input links front panel connector. Each input link has three differential signal pairs for data and one pair for the clock. Link #0 is an exception and has four differential pairs for data and one pair for the clock. On the LVDS cables the center column is connected to the cable shield. The center column of the board connector and all the pins labeled as "IS_GND" are connected to a copper pour that can be left floating, connected to the earth ground (front panel, chassis), or to the mixer board digital ground. The connection between the input links shield ground copper pour and the earth or digital ground can be done placing a solder bridge between two pads on the bottom front corner (solder side) of the mixer board (see Figure 12.1).

| Link# | Pin # | Row ‘a’ | Row ‘b’ | Row ‘c’ | Row ‘d’ | Row ‘e’ |
| --- | --- | --- | --- | --- | --- | --- |
| 15 | 8 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 7 | /D0 | D0 | IS_GND | CLK | /CLK |
| 14 | 6 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 5 | /D0 | D0 | IS_GND | CLK | /CLK |
| 13 | 4 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 3 | /D0 | D0 | IS_GND | CLK | /CLK |
| 12 | 2 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 1 | /D0 | D0 | IS_GND | CLK | /CLK |
| 11 | 25 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 24 | /D0 | D0 | IS_GND | CLK | /CLK |
| 10 | 23 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 22 | /D0 | D0 | IS_GND | CLK | /CLK |
| 9 | 21 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 20 | /D0 | D0 | IS_GND | CLK | /CLK |
| 8 | 19 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 18 | /D0 | D0 | IS_GND | CLK | /CLK |
| 7 | 17 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 16 | /D0 | D0 | IS_GND | CLK | /CLK |
| 6 | 15 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 14 | /D0 | D0 | IS_GND | CLK | /CLK |
| 5 | 13 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 12 | /D0 | D0 | IS_GND | CLK | /CLK |
| 4 | 11 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 10 | /D0 | D0 | IS_GND | CLK | /CLK |
| 3 | 9 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 8 | /D0 | D0 | IS_GND | CLK | /CLK |
| 2 | 7 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 6 | /D0 | D0 | IS_GND | CLK | /CLK |
| 1 | 5 | D1 | /D1 | IS_GND | D2 | /D2 |
|  | 4 | /D0 | D0 | IS_GND | CLK | /CLK |
|  | 3 | D1 | /D1 | IS_GND | D2 | /D2 |
| 0 | 2 | /D0 | D0 | IS_GND | CLK | /CLK |
| (CPS) | 1 | IS_GND | IS_GND | IS_GND | D3 | /D3 |

Table 4.1, Signal assignments for the LVDS inputs connector.

## LVDS Links Outputs to DFEs

The Mixer Board sends the data to the DFE boards over sixteen 28 bit wide LVDS links. The data is transmitted along five differential pair (four data and one clock) on each link. The Mixer Board uses the Texas Instrument [Ref. 38] SN65LVDS93 serializers as transmitters which provide 28 bits of 3.3 V TTL data and clock outputs. The Digital Front-End Board uses the SN65LVDS94 deserializers as receivers.

As was done for the LVDS links’ inputs, special care was taken on the Mixer Board design to ensure that the highest signal integrity is maintained on the LVDS outputs. All traces from the transmitters to the connector are as short as possible and matched in length.

Figure 4.2, LVDS Output links logic block.

Table 4.2 shows the pinout of the output links’ front panel connector. Each output link has four differential signal pairs for data and one differential signal pair for the clock. On the LVDS cables the center column of the connector is connected to the cable shield. The center column of the board connector and all the pins labeled as "OS_GND" are connected to a copper pour that can be left floating, connected to the earth ground (front panel, chassis), or can be connected to the mixer board digital ground. The connection between the output links shield ground copper pour and the earth or digital ground can be done by placing a solder bridge between two pads on the top front corner (solder side) of the mixer board (see Figure 12.1).

The top row of the connector was used in an "after manufacturing" hardware modification to allow front panel access to one of the two programmable logic JTAG chains. This modification allows reprogramming the board controller EEPROM without removing the board from the mixer subrack.

| Link# | Color | Pin # | Row ‘a’ | Row ‘b’ | Row ‘c’ | Row ‘d’ | Row ‘e’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Board Controller JTAG | N.A. | 25 | TMS | TCK | Board digital GND (JTAG cable shield) | TDI | TDO |
|  | Striped | 24 | D1 | /D1 | OS_GND | D2 | /D2 |
| 17 | red | 23 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 22 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 21 | D1 | /D1 | OS_GND | D2 | /D2 |
| 16 | red | 20 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 19 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 18 | D1 | /D1 | OS_GND | D2 | /D2 |
| 15 | blue | 17 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 16 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 15 | D1 | /D1 | OS_GND | D2 | /D2 |
| 14 | yellow | 14 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 13 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 12 | D1 | /D1 | OS_GND | D2 | /D2 |
| 13 | purple | 11 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 10 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 9 | D1 | /D1 | OS_GND | D2 | /D2 |
| 12 | orange | 8 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 7 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 6 | D1 | /D1 | OS_GND | D2 | /D2 |
| 11 | green | 5 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 4 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Striped | 3 | D1 | /D1 | OS_GND | D2 | /D2 |
| 10 | green | 2 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE1) | 1 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  |  | 25 | OS_GND | OS_GND | OS_GND | OS_GND | OS_GND |
|  | Plain | 24 | D1 | /D1 | OS_GND | D2 | /D2 |
| 07 | red | 23 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 22 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 21 | D1 | /D1 | OS_GND | D2 | /D2 |
| 06 | red | 20 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 19 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 18 | D1 | /D1 | OS_GND | D2 | /D2 |
| 05 | blue | 17 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 16 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 15 | D1 | /D1 | OS_GND | D2 | /D2 |
| 04 | yellow | 14 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 13 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 12 | D1 | /D1 | OS_GND | D2 | /D2 |
| 03 | purple | 11 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 10 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 9 | D1 | /D1 | OS_GND | D2 | /D2 |
| 02 | orange | 8 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 7 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 6 | D1 | /D1 | OS_GND | D2 | /D2 |
| 01 | green | 5 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 4 | OS_GND | OS_GND | OS_GND | D3 | /D3 |
|  | Plain | 3 | D1 | /D1 | OS_GND | D2 | /D2 |
| 00 | green | 2 | /D0 | D0 | OS_GND | CLK | /CLK |
|  | (DFE0) | 1 | OS_GND | OS_GND | OS_GND | D3 | /D3 |

Table 4.2, Signal assignments for the LVDS outputs connector.

## LVDS Cabling

The high-speed LVDS links interfacing the Analog Front End Boards with the Mixer System and the Mixer System with Digital Front End Boards use differential pairs parallel custom cables having 100 ( differential impedance. These cables are terminated with lead assemblies to connect to the Mixer Board front panel connectors. The Mixer Board front panel connectors have a 50 ( single ended (signal to ground) and an 89 ( differential (signal to signal) impedance.

Cable characteristics:

Individually Shielded Twisted Pairs. 		Signal and drain conductor size: 28 AWG

Propagation delay: 1.3 ns/ft [4.265 ns/m]	Propagation Velocity: 0.769 ft/ns [0.234 m/ns]

Figure 4.3, LVDS cabling.for a 28 bit wide link.

Figure 4.4, 28 bit link (3x5) LVDS cable.

## Mixer System Backplane

The D0 Mixer System Backplane was developed as an interconnect and power distribution bus for the D0 Mixer Board set. It resembles the VME J1/J2 backplane form, but does not adhere to VME backplane specifications.

The mechanical and electrical specifications are available in separate documents [Ref. 8].

Figure 4.5 shows a sketch of the mixer system backplane.

The backplane supports the following interfaces:

Subrack controller general-purpose bus interface.

Used for configuration download and for remote access to the mixer boards. More details on the bus in paragraph 4.5 (page 29). More information about the Subrack Controller is provided in Paragraph 14.1 (page 139) and in a separate document [Ref. 5e].

Subrack controller slow monitoring serial bus interface.

During data acquisition, due to the proximity of the mixer system to detector components, noise considerations suggested avoiding accessing the mixer system over the "general purpose bus interface". The slow monitoring serial bus provides a way to readback status information from the mixer boards. More details in paragraph 4.6 (page 47).

Subrack controller 1553 interface.

The subrack controller is remotely accessible through a MIL-STD-1553 serial bus. The MIL-STD-1553 is a networking standard used for integration of military platforms [Ref. 42]. The backplane hosts the two 1553 triaxial connectors needed by the subrack controller to implement the 1553 interface.

Board to board buses.

Mixer boards need to exchange part of the data they receive over the LVDS input links with the adjacent boards belonging to the same mixer subsystem (four boards). This is accomplished with two LVTTL parallel buses 41 bit wide, one to the next backplane slot to the left and one to the next backplane slot to the right.

Timing signals distribution

In a mixer subsystem (group of four boards), the leftmost board is used as "master" for distribution of global clock and global SYNC signals to the other three boards (slaves). The clock is distributed over three (one for each slave board) point-to-point LVDS connections. The SYNC is distributed over three point-to-point LVTTL connections.

Power supply.

A mixer board is powered through a backplane connection to the 3.3Volts 240 Ampere subrack power supply. A small brick power supply is used to provide 5 Volts power needed by the subrack controller (slot 1). Two green LEDs, one for each supply voltage are on when the backplane is powered. Three polyfuses are used as over-current protection. Each mixer board has its own over-current/over-voltage protection.

Figure 4.5, Mixer System backplane

## Mixer Board - Subrack Controller General Purpose Bus interface

A general-purpose address/data bus connects the 20 Mixer Boards to the Subrack Controller. The bus has 16 address and 8 data bits. The Subrack Controller is the same used for Digital Front End Subrack [Ref. 5]. Each slot in the Mixer System Subrack is uniquely identified by the 5 bits address provided in Table 4.3. The address bits are hardwired into the backplane (Geographical Addressing) using 5 bits (MOD_ID) allowing each board to be addressed by is location in the subrack.

Figure 4.6, Address bits.

| Slot # | Base Address | Slot MOD_ID | Mixer Board # | Supersector # | Notes [DFE subrack name and slot# on the D0 detector platform] |
| --- | --- | --- | --- | --- | --- |
| 1 | n/a | n/a | - | - | Subrack Controller slot. |
| 2 | 0x02 | b00000 | 1 | 4 (Sectors #1, 2) | Master slot. Feeds DFE #0 [PC03-3 Slot2], DFE#1 [PC03-3 Slot3]. |
| 3 | 0x03 | b00001 | 2 | 4 (Sectors #3, 4) | Slave slot. Feeds DFE #2 [PC03-3 Slot4], DFE#3 [PC03-3 Slot5]. |
| 4 | 0x04 | b00010 | 3 | 4 (Sectors #5, 6) | Slave slot. Feeds DFE #4 [PC03-3 Slot6], DFE#5 [PC03-3 Slot7]. |
| 5 | 0x05 | b00011 | 4 | 4 (Sectors #7, 8). | Slave slot. Feeds DFE #6 [PC03-3 Slot8], DFE#7 [PC03-3 Slot9]. |
| 6 | 0x06 | b00100 | 1 | 5 (Sectors #1, 2) | Master slot. Feeds DFE #8 [PC03-3 Slot10], DFE#9 [PC03-3 Slot11]. |
| 7 | 0x07 | b00101 | 2 | 5 (Sectors #3, 4) | Slave slot. Feeds DFE #10 [PC03-3 Slot12], DFE#11 [PC03-3 Slot13]. |
| 8 | 0x08 | b00110 | 3 | 5 (Sectors #5, 6) | Slave slot. Feeds DFE #12 [PC03-3 Slot14], DFE#13 [PC03-3 Slot15]. |
| 9 | 0x09 | b00111 | 4 | 5 (Sectors #7, 8) | Slave slot. Feeds DFE #14 [PC03-3 Slot16], DFE#15 [PC03-3 Slot17]. |
| 10 | 0x0A | b01000 | 1 | 1 (Sectors #1, 2) | Master slot. Feeds DFE #16 [PC03-3 Slot18], DFE#17 [PC03-3 Slot19]. |
| 11 | 0x0B | b01001 | 2 | 1 (Sectors #3, 4) | Slave slot. Feeds DFE #18 [PC03-3 Slot20], DFE#19 [PC03-3 Slot21]. |
| 12 | 0x0C | b01010 | 3 | 1 (Sectors #5, 6) | Slave slot. Feeds DFE #20 [PC03-2 Slot2], DFE#21 [PC03-2 Slot3]. |
| 13 | 0x0D | b01011 | 4 | 1 (Sectors #7, 8) | Slave slot. Feeds DFE #22 [PC03-2 Slot4], DFE#23 [PC03-2 Slot5]. |
| 14 | 0x0E | b01100 | 1 | 2 (Sectors #1, 2) | Master slot. Feeds DFE #24 [PC03-2 Slot6], DFE#25 [PC03-2 Slot7]. |
| 15 | 0x0F | b01101 | 2 | 2 (Sectors #3, 4) | Slave slot. Feeds DFE #26 [PC03-2 Slot8], DFE#27 [PC03-2 Slot9]. |
| 16 | 0x10 | b01110 | 3 | 2 (Sectors #5, 6) | Slave slot. Feeds DFE #28 [PC03-2 Slot10], DFE#29 [PC03-2 Slot11]. |
| 17 | 0x11 | b01111 | 4 | 2 (Sectors #7, 8) | Slave slot. Feeds DFE #30 [PC03-2 Slot12], DFE#31 [PC03-2 Slot13]. |
| 18 | 0x12 | b10000 | 1 | 3 (Sectors #1, 2) | Master slot. Feeds DFE #32 [PC03-2 Slot14], DFE#33 [PC03-2 Slot15]. |
| 19 | 0x13 | b10001 | 2 | 3 (Sectors #3, 4) | Slave slot. Feeds DFE #34 [PC03-2 Slot16], DFE#35 [PC03-2 Slot17]. |
| 20 | 0x14 | b10010 | 3 | 3 (Sectors #5, 6) | Slave slot. Feeds DFE #36 [PC03-2 Slot18], DFE#37 [PC03-2 Slot19]. |
| 21 | 0x15 | b10011 | 4 | 3 (Sectors #7, 8) | Slave slot. Feeds DFE #38 [PC03-2 Slot20], DFE#39 [PC03-2 Slot21]. |

Table 4.3, Mixer System Subrack slot addressing

All signals used in the Subrack Controller General Purpose Bus interface are pulled to a logic high level on the backplane (see block "termination" in Figure 4.5).

The following description of the backplane General Purpose Bus protocol is partially derived and compliant with specifications in [Ref. 5c].

### Bus Signals

Figure 4.7, General Purpose Bus signals.

The Bus protocol is a simplification of a VME A16D8 bus [Ref. 3].

| Signal |  |
| --- | --- |
| ADDR[15..0] | 16 bit Address bus. ADDR[15..13] unused ADDR[12..8] Base address (slot address) ADDR[7..5] Broadcasting control (write operations only) "000" normal addressing (one board at the time) "001" Subsystem/Super Sector Broadcasting (all board belonging to the Subsystem/Super Sector) "010" Mixer Board # Broadcasting (all boards having the same position in the five Subsystems/Super Sectors) "100" Subrack broadcasting (all boards) Any other set is not recognized (boards will not respond). ADDR[4..0] Register address |
| /SYSRST | Active low signal. Force all the Mixer boards in a power-up reset state if asserted for more then 2 seconds. NOT IMPLEMENTED. |
| SYSCLK | Free running clock with a maximum frequency of 12 MHz. Can be shut down by the subrack controller. |
| AS | Address Valid signal. Indicate that the address on the bus is valid on the next rising edge of SYSCLK. |
| WRITE | Active high (controller writing data to a Mixer Board). |
| DATA[7..0] | 8 bit Data bus. |
| /DTACK | Data Transfer Acknowledge. Active low, open drain signal. |
| /BERR | Bus Error. Active low, open drain signal. NOT IMPLEMENTED. |

Table 4.4, General Purpose Bus signals.

The Subrack Controller general purpose A16:D8 bus is synchronous, all the signals are registered using SYSCLK. To comply with timing specifications the logic on the mixer board uses both the rising and the falling edge of SYSCLK to register signals.

### Write and Read Cycles

The mixer board latchs the address and data lines on the rising edge of SYSCLK when the Address Strobe (AS) signal is high. The address is then compared with the geographical address of the board. For write operations, the address comparison will take into account the content of the value of the three bits (ADDR[7..5]) used for broadcasting operations (see Table 4.4). If the address is recognized as valid (i.e. as belonging to the board addressable space) the mixer board  will respond on the next SYSCLK falling edge driving the Data Transfer Acknoledge (DTACK) signal low for one clock cycle. During broadcasting operations every board addressed by the broadcast will respond.

The mixer board addressable space is larger than the actual space used for data registers, and some of the data registers and register bits are read-only. The write operation will have an effect only if the data register addressed exists inside the addressable space, and only on the bits of this register which are writable.

Figure 4.8, Write operation timing

For read operations the data is made available for the duration of one clock cycle on the first SYSCLK falling edge after a valid address has been received. At the same time, and still for one clock cycle the board will pull down the Data Transfer Acknowledge. Read operations to parts of the addressable space that is not implemented will return invalid data. Read operation addressing vacant subrack slots will return 0x00. Read operations do not support broadcasting.

Figure 4.9, Read operation timing

### Data Space Description

The Mixer Board provides 32 8-bit wide register locations in data space as described in the following subsections. Some register locations of the data space are not currently implemented. Table 4.5 shows the data space address map. The following description of the data space is in part derived from [Ref.5a].

| Register | Access | Register Address (5 bits) |
| --- | --- | --- |
| (0) Board Status/Control register | Read/Write | 0x00 |
| (1) Device Status Control register | Read/Write | 0x01 |
| (2) Device Configuration Data register ☼ | Read/Write | 0x02 |
| (3) Device Firmware ID register | Read/Write | 0x03 |
| (4) Mode of Operation register | Read/Write | 0x04 |
| (5) Input Links Error Status Low register | Read | 0x05 |
| (6) Input Links Error Status High register | Read | 0x06 |
| (7) Device Access-Address register ☼ | Read/Write | 0x07 |
| (8) Device Access-Data register ☼ | Read/Write | 0x08 |
| (9) DFE0 Output Links (00, 01, 02, 03, 04, 05, 06, 07) Test Mode register | Read/Write | 0x09 |
| (10) DFE1 Output Links (10, 11, 12, 13, 14, 15, 16, 17) Test Mode register | Read/Write | 0x0A |
| (11) Monitoring Mode register | Read/Write | 0x0B |
| (12) Monitoring Status Low (Green LEDs 0..7) register | Read | 0x0C |
| (13) Monitoring Status High (Green LEDs 8..15) register | Read | 0x0D |
| (14) Monitoring Status Low History (Green LEDs 0..7) register | Read | 0x0E |
| (15) Monitoring Status High History (Green LEDs 8..15) register | Read | 0x0F |
| (16) Board Status/Control register B | Read/Write | 0x10 |
| (17) FIFO Trigger Control register | Read/Write | 0x11 |
| (18 to 21) -- not implemented -- | -- | 0x20..0x15 |
| (23) MMode Control | Read/Write | 0x16 |
| (23) MMode GL | Read/Write | 0x17 |
| (24) MMode GH | Read/Write | 0x18 |
| (25) MMode RL | Read/Write | 0x19 |
| (26) MMode RH | Read/Write | 0x1A |
| (27) Read/Write Test register | Read/Write | 0x1B |
| (28) Firmware revision date DAY register | Read | 0x1C |
| (29) Firmware revision date MONTH register | Read | 0x1D |
| (30) Firmware revision date YEAR register | Read | 0x1E |
| (31) Board serial number register | Read | 0x1F |

☼ writing operations need to be enabled through setting the appropriate bit in the Mode of Operation register.

Table 4.5, Data space address map.

### Board Status/Control register

Relative address 0x00 (5 bits) is the Board Status/Control register, a read/write register.

Figure 4.10, Board Status/Control Register.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..4 | BOARD TYPE CODE | (read only) Used by the DAQ system to recognize the type of board. The mixer board type is "b1101" or "0xD". |
| 3 | Global Clock/SYNC Error history | (read only) Latched version of Global Clock/SYNC Error. It is reset to '0' thorough the Board Status/Control register B (0x10). The bit is not cleared by a board reset because of the time taken by the clock controller logic to re-establish normal operations after a board reset. The bit is reset by writing to the appropriate bit in the “Board Status/Control register B” (0x10). |
| 2 | Global Clock/SYNC Error | (read only) The mixer board automatically chooses most appropriate clock to be used, but for correct operations the mixer subsystem master boards must use the link#0 clock and the mixer subsystem slave boards must use the backplane clock. Furthermore, the link#0 SYNC on the master boards and the backplane SYNC on the slave boards must respect the correct protocol (one and only one high pulse in a seven clock cycles wide window). If these conditions are not satisfied the Global Clock/SYNC Error bit is set. |
| 1 | RESET | (read/write) Writing a “1” will force the board to be reset and to stay in the reset status till the bit is deasserted. Reset will not cause devices to lose their configuration. Reset should be “0” while devices are configured. |
| 0 | READY | (read only) This bit is set if all devices are configured. |

Table 4.6, Board Status/Control Register.

### Device Status/Control register

Relative address 0x01 (5 bits) is the Device Status/Control register, a read/write register. This register allows setting a pointer to one of sixteen FPGAs on the mixer board (not includng the board controller). This pointer is used during device configuration together with the Device Configuration Data register. The pointer is also used in the device access structure (see 4.5.12) to perform read/write operations on registers located inside the FPGAs. This register allow the user to erase/verify devices configuration.

Figure 4.11, Device Status/Control Register.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7 | DONE | (Read only) Goes high when the selected device (through DEVICE SELECT bits) has received all its configuration data. |
| 6 | PROG | (read/write) Used to assert the Mixer Board program bit. Each FPGA has its own program bit. The bit PROG on device #0 (the first device in the programming chain, is Back-End FPGA DFE1 Yellow-Purple) is used to force all the 16 devices of the Mixer Board to erase their configuration memories and preparing to accept new configuration data. This is achieved in two steps: Writing a '1' will erase the configuration memories of all 16 devices/FPGAs, Writing a '0' will make the devices/FPGAs available to receive configuration data. When all devices are configured this bit is no longer accessible for writing unless the appropriate bit is set in the Mode of Operation Register. This is a protection feature to prevent mistakenly erasing the devices configuration memories. |
| 5 | INIT | (Read only) NOT IMPLEMENTED. Read back always ‘1’. |
| 4 | REG | (read only) NOT IMPLEMENTED. Read back always ‘0’. |
| 3..0 | DEVICE SELECT | (Read/Write) Allow selection of one of the 16 Mixer Board's devices: b0000 (0x0) [Device#0] Back End FPGA DFE1 Yellow Purple b0001 (0x1) [Device#1] Back End FPGA DFE1 Blue Red b0010 (0x2) [Device#2] Back End FPGA DFE1 Green Orange b0011 (0x3) [Device#3] Back End FPGA DFE0 Blue Red b0100 (0x4) [Device#4] Back End FPGA DFE0 Green Orange b0101 (0x5) [Device#5] Back End FPGA DFE0 Yellow Purple b0110 (0x6) [Device#6] Front End FPGA Input Links #13..15 b0111 (0x7) [Device#7] Front End FPGA Input Links #4..6 b1000 (0x8) [Device#8] Front End FPGA Input Links #1..3 b1001 (0x9) [Device#9] Front End FPGA Input Links #10..12 b1010 (0xA) [Device#10] Front End FPGA Input Link #0 b1011 (0xB) [Device#11] Back End FPGA Backplane Left Driver b1100 (0xC) [Device#12] Front End FPGA Input Links #7..9 b1101 (0xD) [Device#13] Back End FPGA Backplane DFE0 Receiver b1110 (0xE) [Device#14] Back End FPGA Backplane DFE1 Receiver b1111 (0xF) [Device#15] Back End FPGA Backplane Right Driver |

Table 4.7, Device Status/Control Register.

### Device Configuration Data register

Relative address 0x02 (5 bits) is the Device Configuration Data register, a read/write register.

Figure 4.12, Device Configuration Data Register

Configuration data bytes are written to this register. Bit 7 is the most significant bit (MSb) and bit 0 is the Least Significant bit (LSb). The board controller will route the configuration data to the device selected as "current device" using the Device Status/Control register. Device configurations is lost if the board is powered down or the PROG bit of the Device Status/Control Register is set high for device#0 (Back-End FPGA DFE1 Yellow-Purple). When all devices are configured, the Device Configuration Register is no longer accessible for writing unless the appropriate bit is set in the Mode of Operation Register.

### Device Firmware ID register

Relative address 0x03 (5 bits) is the Device Firmware ID register, a read/write register.

Figure 4.13, Firmware ID Register.

This register is used to store the firmware id assigned to each of the fifteen devices during the configuration process. This register provides the firmware id of the device pointed to by the Device Status/Control Register. The firmware id is specified in the "Configure Device" DFE Controller command used to download the configuration file to each FPGA. The only time when this register is writable is when the device is not configured (DONE signal low).

The device firmware id information, as is devices configuration, is lost if the board is powered down or if the PROG bit of the Device Status/Control register is set high for device#0.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Device Firmware ID | ID byte assigned to the device when it was configured. It can only be written before the configuration process when the device is not yet configured. After device configuration the register is read only. |

Table 4.8, Device Firmware ID Register.

### Mode of Operation register

Relative address 0x04 (5 bits) is the Mode of Operation register, a read/write register.

The Mode of Operation register allows for activation/control of some of the board features.

Figure 4.14, Mode of Operation register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7 | -- | Not used. |
| 6 | -- | Not used. |
| 5 | -- | Not used. |
| 4 | Enable LVDS TXs Clock | Turns ON the PLL driving the clock to the LVDS Transmitters. Default is enabled ('1'). |
| 3 | Enable Erasing of Device Configuration | Default is disabled ('0'). Independently from the value of this bit devices configuration/erasing is always possible until all the devices have been configured. When all device are configured, the only way to reconfigure them is to set this bit to '1' and erase their configuration using the PROG bit in the Device Status/Control register. |
| 2 | Enable Device Access Registers | Enable the Device Access Registers. Default is disabled ('0'). |
| 1 | LED Monitoring Mode | Enable LEDs to display the monitoring mode when the mode is changed. Default is enabled ('1'). |
| 0 | Enable latching in the Input Links Error Status registers | Enable to latch the errors in the Input Links Error Status registers (0x05 and 0x06). Default is disabled (‘0’). |

Table 4.9, Mode of Operation Register.

### Input Links Error Status registers

Relative address 0x05 (5 bits) is the Input Links Error Status Low register, relative address 0x06 (5 bits) is the Input Links Error Status High register, both are read only registers. These two registers provide an easy way to monitor the status of the LVDS input links. The error information reported by these two registers can be latched setting the "Enable latching in the Input Links Error Status registers" bit to ‘1’ in the Mode of Operation register (Paragraph 4.5.8).

The status of the input links can also be monitored selecting monitoring mode #14 in the Monitoring Mode register (Paragraph 4.5.14). Monitoring Mode #14 utilize the same signals used by the Input Links Status registers but is not affected by the "enable latching" feature.

Figure 4.15, Input Links Error Status Registers

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Link Status | Status of the input links #7 (bit 7) to #0 (bit 0). A high value ('1') indicates that the corresponding input link has one of the following critical errors: Link clock: missing or out of frequency range (45MHZ to 55MHz) or Delay Locked Loop not locked; Link frame marker (SYNC) before synchronization: missing or not respecting the protocol (one and only one high bit every seven clock cycles); Link frame marker (SYNC) after synchronization: missing or not respecting the protocol (one and only one high bit every seven clock cycles); Link frame synchronization: the frames are not synchronized with those of the reference link (usually link#0 on the first board (master) in the mixer subsystem (group of four boards handling the data from one supersector)). |

Table 4.10, Input Links Error Status Low Register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Link Status | Status of the input links #15 (bit 7) to #8 (bit 0). A high value ('1') indicates that the corresponding input link has one of the critical errors mentioned in the input links status high register description. |

Table 4.11, Input Links Error Status High Register

### Device Access-Address register

Relative address 0x07 (5 bits) is the Device Access-Address register, a read/write register. Operations on this register are disabled until all devices are configured ("READY" signal from Board Status/Control register is active). Furthermore, the Device Access feature needs to be enabled by setting the appropriate bit in the Mode of Operation register.

Figure 4.16, Device Access-Address register

The Device Access-Address register is part of the structure that allows access to advanced diagnostic features of the Mixer Board. This register contains the pointer to the device's registers (device's register address). Each time the Device Access-Address register is accessed in writing, the value is also written in each device internal register's pointer. The register pointed to by the Device Access-Address register is accessible thorough the Device Access Data register.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Device Access-Address | Pointer to device's registers. |

Table 4.12, Device Access-Address register.

### Device Access-Data register

Relative address 0x08 (5 bits) is the Device Access Data register, a read/write register. Operations on this register are disabled until all devices are configured ("READY" signal from Board Status/Control register is active). Furthermore, the Device Access feature needs to be enabled by setting the appropriate bit in the Mode of Operation register.

Figure 4.17, Device Access Data register

The Device Access-Data register is part of the structure that allows access to advanced diagnostic features of the Mixer Board. It contains the data of read/write operations performed on device's registers. To access a particular register, two pointers are needed; the device accessed is the one pointed by the Device Status/Control register, the register on the accessed device is the one pointed to by the Device Access Address register.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Device Access Data | Device's internal register data. |

Table 4.13, Device Access register.

### Device Access Structure

The Device Access-Address and Device Access-Data registers allow for access to advanced diagnostic features of the Mixer Board. In order to access these features a good understanding of the mixer board/system operation is required.

Each mixer board has 17 devices, one of them is the board controller which is the device hosting the backplane interface. There are two type of board registers, one is located on the board controller; the second type of registers are residing in all the other devices. The procedure to access the two types of registers is different. The board controller registers are accessible with a single (write or read) subrack controller command.

The way to operate on registers not residing on the board controller is different. The procedure includes the use of three support registers on the board controller itself. A register is used to point to the device to be accessed (Device Status/Control register), one to point to the location to be accessed inside the desired device (Device Access Address register) and one as data register (Device Access Data register). As safety precaution the device access features need to be enabled by setting the appropriate bit in the Mode of Operation register.

Figure 4.18, Device Access Structure

The multiplexer shown in Figure 4.18 is actually part of each device, so when writing to the Device Access Address register the device register pointer data is automatically written through the board’s local bus to a register in each of the sixteen devices and is used in each of them to control the multiplexer. This implies that when changing the Device Select (Device Status/Control register) to point to a different device there is no need to change the device register pointer (Device Access Address register) if the register pointed is the same in both devices. The devices internal registers are listed and described in Paragraph 7.

### Output Links Test Mode registers

Relative address 0x09 (5 bits) is the DFE0 Output Links Test Mode register. Relative address 0x0A (5 bits) is the DFE1 Output Links Test Mode register. Both are read/write registers. These two registers allow the enabling of test pattern transmission on the output LVDS links. The test pattern consists of a walking one sequence followed by a coded word containing information that uniquely identifies the link in a mixer subsystem (4 mixer boards). The test pattern used is specified in Paragraph 11 (Page 112). The pattern is repeated continuously and its starting point is synchronized on the sixteen output links of a mixer board. The status of an output link (test pattern enabled or disabled) can be monitored selecting monitoring mode #13 in the Monitoring Mode register (Paragraph 4.5.14).

Figure 4.19, DFE0 and DFE1 Output Links Test Mode Registers

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..6 | -- | Not used. |
| 5 | Links 06, 07 TM Enable | Enable test pattern transmission on the DFE0 Red Links (06, 07) |
| 4 | Link 05 TM Enable | Enable test pattern transmission on the DFE0 Blue Link (05) |
| 3 | Link 04 TM Enable | Enable test pattern transmission on the DFE0 Yellow Link (04) |
| 2 | Link 03 TM Enable | Enable test pattern transmission on the DFE0 Purple Link (03) |
| 1 | Link 02 TM Enable | Enable test pattern transmission on the DFE0 Orange Link (02) |
| 0 | Links 00, 01 TM Enable | Enable test pattern transmission on the DFE0 Green Links (00, 01) |

Table 4.14, DFE0 Output Links Test Mode Register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..6 | -- | Not used. |
| 5 | Links 16, 17 TM Enable | Enable test pattern transmission on the DFE1 Red Links (16, 17) |
| 4 | Link 15 TM Enable | Enable test pattern transmission on the DFE1 Blue Link (15) |
| 3 | Link 14 TM Enable | Enable test pattern transmission on the DFE1 Yellow Link (14) |
| 2 | Link 13 TM Enable | Enable test pattern transmission on the DFE1 Purple Link (13) |
| 1 | Link 12 TM Enable | Enable test pattern transmission on the DFE1 Orange Link (12) |
| 0 | Links 10, 11 TM Enable | Enable test pattern transmission on the DFE1 Green Links (10, 11) |

Table 4.15, DFE1 Output Links Test Mode Register

### Monitoring Mode register

Relative address 0x0B (5 bits) is the Monitoring Mode register, a read/write register. This register allows changing of the monitoring mode, which allows the user to select the set of signals that are driving the front panel LEDs (see Paragraph 6.1 for a description of the monitoring modes). The status of these signals can also be remotely read by accessing the Monitoring Status register (Paragraph 4.5.15). Information about whether the monitored signals are changing or have changed are stored in the Monitoring Mode Status History registers (Paragraph 4.5.16). Accessing the Monitoring Mode register in writing will reset the two Monitoring Status History registers. It should be noted that the monitoring mode can also be changed using the front panel reset button. Each time the button is pressed for less then two seconds, the board switches to the next monitoring mode. This change is automatically reflected in the content of the Monitoring Mode register.

Each front panel LED consists of a green and a red LED in the same package. The LED latch mode feature allows latching the LED in the ON position when they get driven.

The LED monitor set feature is used to select between the green and the red sets of LED as trigger signals for the Monitoring Status and Monitoring Status History registers (Paragraphs 4.5.15 and 4.5.16).

Figure 4.20, Monitoring Mode Register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7 | -- | Not used. |
| 6 | Mode 15 LEDs ON/OFF | In Monitoring Mode #15 all LEDs are on by default ('0'). When this bit is set high ('1') all the LEDs will be forced to be OFF in Monitoring Mode #15. |
| 5 | LED monitor set | Used to select the set of led to monitor through the monitoring status registers. '0': green LEDs set (default). '1' red LEDs set. |
| 4 | Enable LED Latch Mode | When enabled will force the LEDs (both red and green) to remain ON when they are turned ON even by a short transition. This "LED latching" is reset every time the Monitoring mode is changed (through the monitoring mode register or using the front panel reset button) or when the monitoring mode register is accessed in writing. Default is disabled ('0'). |
| 3..0 | Monitoring Mode Select | Allows for selection of the monitoring mode |

Table 4.16, Monitoring Mode Register

### Monitoring Status registers

Relative address 0x0C (5 bits) is the Monitoring Status Low register, and relative address 0x0D (5 bits) is the Monitoring Status High register. Both are read only registers. These registers allow for reading the current status of the front panel LEDs. The default set of LEDs read is the green one. The Monitoring Mode register (Paragraph 4.5.14) allows switching to the red LED set. The front panel LEDs reflect the status of different groups of signals on the mixer board depending of which is the current monitoring mode. The monitoring mode can be changed using the front panel reset button (pressing it for less then 2 seconds) or remotely by accessing the Monitoring Mode register. The sixteen available monitoring modes are described in Paragraph 6.1.

Figure 4.21, Monitoring Status Registers

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Green/Red LEDs #7 to #0 status | Status of the Green/Red LEDs #7 to #0. LED ON is '1', LED OFF is '0'. |

Table 4.17, Monitoring Status Low Register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Green/Red LEDs #15 to #8 status | Status of the Green/Red LEDs #15 to #8. LED ON is '1', LED OFF is '0'. |

Table 4.18, Monitoring Status High Register

### Monitoring Status History registers

Relative address 0x0E (5 bits) is the Monitoring Status Low History register, and relative address 0x0F (5 bits) is the Monitoring Status High History register. Both are read only registers. The bits in these registers are set if the signal driving the corresponding LED has changed status (high to low or low to high) since the last time the registers were reset. The registers are reset each time the Monitoring Mode register is accessed in writing.

Figure 4.22, Monitoring Status History Registers

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Green-Red LED #7 to #0 status history | Status history of the Green-Red LEDs #7 to #0. '1' mean that the signal driving the corresponding Green-Red LEDs changed status since last reset of the register, '0' otherwise. |

Table 4.19, Monitoring Status Low History Register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..0 | Green-Red LED #15 to #8 status history | Status history of the Green-Red LEDs #15 to #8. '1' mean that the corresponding Green-Red LED changed status since last reset of the register, '0' otherwise. |

Table 4.20, Monitoring Status High History Register

### Board Status/Control register B

Relative address 0x10 (5 bits) is the Device Status/Control register B, a read/write register. This register is used to erase the Clock/SYNC error history bit in the Device Status Control register (0x00).

Figure 4.23, Board Status/Control Register B.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..1 | -- | Not used. |
| 0 | Reset Global Clock/SYNC error history. | (read/write) Used to reset the Global Clock/SYNC Error History in the Board Status/Control register A (0x00). This is achieved in one step operation, writing a ‘1’ will reset the history bit in the Board Status/Control register A. The bit always readback ‘0’. |

Table 4.21, Board Status/Control Register B.

### FIFO Trigger Control register

Relative address 0x11 (5 bits) is the FIFO Trigger Control register, a read/write register. This register is used to trigger the Output Links FIFOs. The trigger signal operates simultaneously on all the FIFOs on a Mixer Board. FIFO behavior (FIFO enable, FIFO deepness, content, ..) is controlled by registers in the back end devices (see paragraph 7.3). The trigger signal is internally synchronized with the frame marker of the output link data in order to last only an integer number of frames.

Figure 4.24, FIFO Trigger Control Register.

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..4 | Trigger Length | The number of frames (one frame is seven 53MHz clock cycles long) the trigger should last. |
| 3..2 | -- | Not used. |
| 1 | Continuous Trigger | Used to have a trigger that will last as long as the FIFO Trigger bit is active (high). |
| 0 | FIFO Trigger | A transition from ‘0’ to ‘1’ of this bit will internally latch the other bits in the register and generate a trigger signal for the output links FIFOs. If the “Continuous Trigger” bit is ‘1’ the trigger will last until the “FIFO Trigger” bit is set back to ‘0’. If the “Continuous Trigger” bit is ‘0’ the trigger will last the number of frames specified by the “Trigger Length” bits. For a new trigger to be produced the “FIFO Trigger” bit should be set back to ‘0’ and then to ‘1’ to generate a new ‘0’ to ‘1’ transition. |

Table 4.22, FIFO Trigger Control Register.

### Read/Write Test register

Relative address 0x1B is the read/write test register. This register doesn't affect/reflect the status of the board. Its only purpose is to allow test of read/write operations.

### Firmware Revision Date registers

Relative addresses 0x1C, 0x1D, and 0x1E (5 bits) are the firmware revision date registers; all three are read only registers. These registers contain the Binary Coded Decimal of the day (0x1C), the month (0x1D) and the year (0x1E) of the board controller firmware revision.

### Board Serial Number register

Relative address 0x1F (5 bits) is the board serial number register. It contains the Binary Coded Decimal serial number of the board. As of today, 25 boards have been manufactured. 0x00 is used for boards on which the serial number has not been encoded in the firmware. Board #01 and 02 are the two mixer board prototypes. Because their difference with the production boards are minimal there are no restriction for their use in the mixer system.

The serial number is also marked on the solder side of each board.

## Mixer Board - Subrack Controller Slow Monitoring Serial Bus interface

The following description of the slow monitoring custom serial bus is partially derived from [Ref.5d].

The Mixer system uses several components and signal protocols designed/used by the Digital Front-End Board system. The slow monitoring custom serial bus is one of them.

To reduce noise injection in sensible detector parts located close to the Mixer System the custom general purpose A16:D8 bus is not used during data taking. Status information can be collected from the Mixer Board using a custom serial bus and the information is made accessible trough a MIL-STD-1553 Remote Terminal in the Subrack Controller.

Figure 4.25, Slow Monitoring Bus signals

The subrack controller continuously collect sixteen bits of data from each Mixer Board slow monitoring register.

Figure 4.26, Slow Monitoring Bus register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 15..12 | Board Type | From Board Status/Control Register. Used by the DAQ system to recognize the type of board. The mixer board type is "b1101" or "0xD". |
| 11 | Global Clock./SYNC Error history | From Board Status/Control Register. Latched version of Global Clock./SYNC Error. |
| 10 | Global Clock./SYNC Error | From Board Status/Control Register. The mixer board automatically most appropriate clock to be used, but for correct operations the mixer subsystem master boards must use the link#0 clock and the mixer subsystem slave boars must use the backplane clock. Furthermore the link#0 SYNC on the master boards and the backplane SYNC on the slave boards must respect the correct protocol (one and only one high pulse in a seven clock cycles wide window). If these conditions are not satisfied the Global Clock/SYNC bit is set. |
| 9 | Ready | From Board Status/Control Register. This bit is set if all devices are configured. |
| 8 | Input Links Error | Logic OR of all the bits of the Input Links Error Status registers. |
| 7 | Not Standard Mode | Set when the board is not operating in the standard mode. Is the logic OR of the following signals: not READY (from Board Status/Control Register) not Enable LVDS TXs Clock (from Mode of Operation register) Enable Erasing of Device Configuration (from Mode of Operation register) Enable Device Access Register (from Mode of Operation register) bits 5..0 of the DFE0 Output Links Test Mode register bits 5..0 of the DFE1 Output Links Test Mode register |
| 6 | LED History Status | Logic OR of all the bits of the two LEDs Status History Registers. |
| 5 | LED Status | Logic AND of all the bits of the two LEDs Status Registers. |
| 4 | LED Latch Mode Enable | From Monitoring Mode Register. LED Latch Mode Enable. |
| 3..0 | LED Monitoring Mode | From Monitoring Mode Register. Shows the current LED monitoring mode. |

Table 4.23, Slow Monitoring Bus Register

## JTAG Interface

See a description of JTAG in Paragraph 16. Two four pin Test Access Ports (TAP) are provided on the Mixer Board, the first (Table 4.24) accesses the Board Controller FPGA and its configuration EEPROM, the second (Table 4.25) accesses the chain formed by the remaining sixteen FPGAs.

Figure 4.27, JTAG Connectors pinout

The JTAG Chain#1 TAP has been wired to the front panel top row of pins of the output links connector with a hardware modification. This change allows for board controller EEPROM reprogramming in-system without the need to disconnect the LVDS cabling and to remove the board from the mixer subrack. The front panel pinout is shown in Table 4.2. The JTAG ports have been extensively used during the initial board testing to program the board FPGAs without the need for using the backplane A16:D8 General Purpose bus.

| JTAG Chain#1, connector CON3 |
| --- |
| Device # | Device Type | Notes |
| 1 | XC18V01SO20C | In-System-Programmable Configuration PROM. |
| 2 | XCS40XL-5PQ240C | Spartan-XL FPGA used as Board Controller. |

Table 4.24, JTAG Chain#1 Devices

| JTAG Chain#2, connector CON1 |
| --- |
| Device # | Device Type | Notes |
| 1 | XCS40XL-5PQ240C | U2, Spartan-XL FPGA used as DFE1 Yellow Purple (Outlink 5). |
| 2 | XCS40XL-5PQ240C | U1, Spartan-XL FPGA used as DFE1 Red Blue (Outlink 6). |
| 3 | XCS40XL-5PQ240C | U10, Spartan-XL FPGA used as DFE1 Orange Green (Outlink 4). |
| 4 | XCS40XL-5PQ240C | U11, Spartan-XL FPGA used as DFE0 Red Blue (Outlink 3). |
| 5 | XCS40XL-5PQ240C | U19, Spartan-XL FPGA used as DFE0 Orange Green (Outlink 1). |
| 6 | XCS40XL-5PQ240C | U18, Spartan-XL FPGA used as DFE0 Yellow Purple (Outlink 2). |
| 7 | XCV50-6PQ240C | U31, Virtex FPGA used as LINK_IN 13-15. |
| 8 | XCV50-6PQ240C | U45, Virtex FPGA used as LINK_IN 4-6. |
| 9 | XCV50-6PQ240C | U46, Virtex FPGA used as LINK_IN 1-3. |
| 10 | XCV50-6PQ240C | U32, Virtex FPGA used as LINK_IN 10-12. |
| 11 | XCV50-6PQ240C | U47, Virtex FPGA used as LINK_IN 0. |
| 12 | XCV50-6PQ240C | U48, Virtex FPGA used as Backplane Left Driver. |
| 13 | XCV50-6PQ240C | U33, Virtex FPGA used as LINK_IN 7-9. |
| 14 | XCV50-6PQ240C | U12, Virtex FPGA used as Backplane DFE0 receiver. |
| 15 | XCV50-6PQ240C | U5, Virtex FPGA used as Backplane DFE1 receiver. |
| 16 | XCV50-6PQ240C | U6, Virtex FPGA used as Backplane Right Driver. |

Table 4.25, JTAG Chain#2 Devices

The JTAG ports also allow the performing of a boundary scan [Ref. 17] of the mixer board. The boundary scan testing has proven to be an invaluable resource in the detection of board defects or assembly problems [Ref. 8c]. Table 4.26 lists the Boundary Scan Description Language (BSDL) files for the devices used on the mixer board, which are compatible with JTAG/IEEE 1149.1. The files in Table 4.26 are available from Xilinx [Ref. 40].

| Device | Description | BSDL File |
| --- | --- | --- |
| XCS40XL | Spartan-XL FPGA | xcs40xl_pq240.bsd |
| XCV50 | Virtex FPGA | xcv50_pq240.bsd |
| XC18V512 | In-System-Programmable Configuration PROM. | xc18v512_so20.bsd |

Table 4.26, Boundary Scan Description Language (BSDL) Files

## Logic Analyzer Connectors

For debugging/diagnostic purposes the Mixer Board has three Amp "Mictor 38" connectors (AMP 2-767004-2) to fit the Agilent (formerly HP) [Ref. 11] High Density adapter cables (Agilent E5346A). Each adapter cable fits two test pods of an Agilent 16550A Logic Analyzer allowing monitoring of 32 signals. The following three tables list the signals connected to each mixer board's logic analyzer connector. There are several spare connections that can be assigned in the FPGA hardware description (VHDL code) to monitor specific signals. These spare connections are marked with .

| Notes | Schematic name | Pin # | Pin name | Pin name | Pin # | Schematic name | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | N.C. | 1 ▬ | +5VDC | SCL | ▬ 2 | N.C. |  |
|  | GND | 3 ▬ | GND | SDA | ▬ 4 | N.C. |  |
|  | N.C. | 5 ▬ | CLK1 | CLK2 | ▬ 6 | N.C. |  |
| A16:D8 bus SYStem CLocK | SYSCLK | 7 ▬ | P1.15 | P2.15 | ▬ 8 | BADDR15 | A16:D8 bus Address bit |
| A16:D8 bus Address Strobe | AS | 9 ▬ | P1.14 | P2.14 | ▬ 10 | BADDR14 | A16:D8 bus Address bit |
| A16:D8 bus /SYStem RESET | /SYSRESET | 11 ▬ | P1.13 | P2.13 | ▬ 12 | BADDR13 | A16:D8 bus Address bit |
| A16:D8 bus WRITE | WRITE | 13 ▬ | P1.12 | P2.12 | ▬ 14 | BADDR12 | A16:D8 bus Address bit |
| A16:D8 bus Data Transfer ACKnoledge | DTACK | 15 ▬ | P1.11 | P2.11 | ▬ 16 | BADDR11 | A16:D8 bus Address bit |
| A16:D8 bus Bus Error | BERR | 17 ▬ | P1.10 | P2.10 | ▬ 18 | BADDR10 | A16:D8 bus Address bit |
| Serial Bus Data In | STAT | 19 ▬ | P1.09 | P2.09 | ▬ 20 | BADDR9 | A16:D8 bus Address bit |
| Serial Bus Clock | IN_STAT-CLK | 21 ▬ | P1.08 | P2.08 | ▬ 22 | BADDR8 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT7 | 23 ▬ | P1.07 | P2.07 | ▬ 24 | BADDR7 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT6 | 25 ▬ | P1.06 | P2.06 | ▬ 26 | BADDR6 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT5 | 27 ▬ | P1.05 | P2.05 | ▬ 28 | BADDR5 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT4 | 29 ▬ | P1.04 | P2.04 | ▬ 30 | BADDR4 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT3 | 31 ▬ | P1.03 | P2.03 | ▬ 32 | BADDR3 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT2 | 33 ▬ | P1.02 | P2.02 | ▬ 34 | BADDR2 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT1 | 35 ▬ | P1.01 | P2.01 | ▬ 36 | BADDR1 | A16:D8 bus Address bit |
| A16:D8 bus Data bit | BDAT0 | 37 ▬ | P1.00 | P2.00 | ▬ 38 | BADDR0 | A16:D8 bus Address bit |

Table 4.27, HP Logic Analyzer connector J3 (suggested analyzer pods: 1 and 2)

| Notes | Schematic name | Pin # | Pin name | Pin name | Pin # | Schematic name | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | N.C. | 1 ▬ | +5VDC | SCL | ▬ 2 | N.C. |  |
|  | GND | 3 ▬ | GND | SDA | ▬ 4 | N.C. |  |
|  | N.C. | 5 ▬ | CLK1 | CLK2 | ▬ 6 | N.C. |  |
| A16:D8 bus Data Buffer Direction | VDAT_DIR | 7 ▬ | P1.15 | P2.15 | ▬ 8 | FPGACLK10 | Board Controller Global Clock |
| A16:D8 bus Data Buffer Enable | /VDAT_EN | 9 ▬ | P1.14 | P2.14 | ▬ 10 | 53CLK0 | Local Oscillator 53MHz Clock |
| Board Controller Master Reset to FPGAs | /MRESET | 11 ▬ | P1.13 | P2.13 | ▬ 12 | ASTRB | Local Bus Address Strobe |
| FE FPGA IN0 | SPFE0_2 | 13 ▬ | P1.12 | P2.12 | ▬ 14 | DSTRB | Local Bus Data Strobe |
| FE FPGA IN0 | SPFE0_1 | 15 ▬ | P1.11 | P2.11 | ▬ 16 | /WRITE | Local Bus /WRITE |
| FE FPGA IN0 | SPFE0_0 | 17 ▬ | P1.10 | P2.10 | ▬ 18 | /CONFIGDAT_EN | Local Bus Buffer enable |
| Backplane DFE1 Rx | SP1RX1 | 19 ▬ | P1.09 | P2.09 | ▬ 20 | CONFIGDAT_DIR | Local Bus Buffer Direction |
| Backplane DFE1 Rx | SP1RX0 | 21 ▬ | P1.08 | P2.08 | ▬ 22 | CONFIGCLK | FPGAs Configuration Clock |
| Backplane DFE0 Rx | SP0RX1 | 23 ▬ | P1.07 | P2.07 | ▬ 24 | FDAT7 | Local Bus Data bit |
| Backplane DFE0 Rx | SP0RX0 | 25 ▬ | P1.06 | P2.06 | ▬ 26 | FDAT6 | Local Bus Data bit |
| Backplane Left Driver | SPLDR1 | 27 ▬ | P1.05 | P2.05 | ▬ 28 | FDAT5 | Local Bus Data bit |
| Backplane Left Driver | SPLDR0 | 29 ▬ | P1.04 | P2.04 | ▬ 30 | FDAT4 | Local Bus Data bit |
| Backplane Right Driver | SPRDR3 | 31 ▬ | P1.03 | P2.03 | ▬ 32 | FDAT3 | Local Bus Data bit |
| Backplane Right Driver | SPRDR2 | 33 ▬ | P1.02 | P2.02 | ▬ 34 | FDAT2 | Local Bus Data bit |
| Backplane Right Driver | SPRDR1 | 35 ▬ | P1.01 | P2.01 | ▬ 36 | FDAT1 | Local Bus Data bit |
| Backplane Right Driver | SPRDR0 | 37 ▬ | P1.00 | P2.00 | ▬ 38 | FDAT0 | Local Bus Data bit |

Table 4.28, HP Logic Analyzer connector J5 (suggested analyzer pods: 3 and 4)

| Notes | Schematic name | Pin # | Pin name | Pin name | Pin # | Schematic name | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | N.C. | 1 ▬ | +5VDC | SCL | ▬ 2 | N.C. |  |
|  | GND | 3 ▬ | GND | SDA | ▬ 4 | N.C. |  |
|  | N.C. | 5 ▬ | CLK1 | CLK2 | ▬ 6 | N.C. |  |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGAs | Analyzer15 | 7 ▬ | P1.15 | P2.15 | ▬ 8 | Analyzer31 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGA | Analyzer14 | 9 ▬ | P1.14 | P2.14 | ▬ 10 | Analyzer30 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGA | Analyzer13 | 11 ▬ | P1.13 | P2.13 | ▬ 12 | Analyzer29 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGA | Analyzer12 | 13 ▬ | P1.12 | P2.12 | ▬ 14 | Analyzer28 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGA | Analyzer11 | 15 ▬ | P1.11 | P2.11 | ▬ 16 | Analyzer27 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGA | Analyzer10 | 17 ▬ | P1.10 | P2.10 | ▬ 18 | Analyzer26 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Blue Red FPGA | Analyzer9 | 19 ▬ | P1.09 | P2.09 | ▬ 20 | Analyzer25 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Yellow Purple FPGA | Analyzer8 | 21 ▬ | P1.08 | P2.08 | ▬ 22 | Analyzer24 | LinkIn0 FE FPGA & DFE1 Blue Red FPGA |
| LinkIn0 FE FPGA & DFE0 Yellow Purple FPGA | Analyzer7 | 23 ▬ | P1.07 | P2.07 | ▬ 24 | Analyzer23 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer6 | 25 ▬ | P1.06 | P2.06 | ▬ 26 | Analyzer22 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer5 | 27 ▬ | P1.05 | P2.05 | ▬ 28 | Analyzer21 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer4 | 29 ▬ | P1.04 | P2.04 | ▬ 30 | Analyzer20 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer3 | 31 ▬ | P1.03 | P2.03 | ▬ 32 | Analyzer19 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer2 | 33 ▬ | P1.02 | P2.02 | ▬ 34 | Analyzer18 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer1 | 35 ▬ | P1.01 | P2.01 | ▬ 36 | Analyzer17 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |
| LinkIn0 FE FPGA & DFE0 Green Orange FPGA | Analyzer0 | 37 ▬ | P1.00 | P2.00 | ▬ 38 | Analyzer16 | LinkIn0 FE FPGA & DFE1 Green Orange FPGA |

Table 4.29, HP Logic Analyzer connector J7 (suggested analyzer pods: 5 and 6)

The signals monitored through connector J7 can be remotely changed to two preset configurations without the need of changing the firmware. The active configuration is determined by a bit in the Input Link Control register (Paragraph 7.1.4).

The LVDS receiver used for the input link#0 is a 28-bit receiver. This type of receiver can also be used as a 21-bit receiver. The two preset configuration for analyzer connector J7 allows monitoring the outputs of the LVDS receiver in both cases, allowing analyzer access to both the 21-bit and the 28-bit LVDS transmissions.

| Notes [schematic name of monitored signal] | Schematic name | Pin # | Pin name | Pin name | Pin # | Schematic name | Notes [schematic name of monitored signal] |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | N.C. | 1 ▬ | +5VDC | SCL | ▬ 2 | N.C. |  |
|  | GND | 3 ▬ | GND | SDA | ▬ 4 | N.C. |  |
|  | N.C. | 5 ▬ | CLK1 | CLK2 | ▬ 6 | N.C. |  |
| Link0 Data bit 15 [Link0_in(20)] | Analyzer15 | 7 ▬ | P1.15 | P2.15 | ▬ 8 | Analyzer31 | Link#0 clock [RXCLK0] |
| Link0 Data bit 14 [Link0_in(19)] | Analyzer14 | 9 ▬ | P1.14 | P2.14 | ▬ 10 | Analyzer30 | Global clock [CLK] |
| Link0 Data bit 13 [Link0_in(18)] | Analyzer13 | 11 ▬ | P1.13 | P2.13 | ▬ 12 | Analyzer29 | Global SYNC [GSYNC] |
| Link0 Data bit 12 [Link0_in(15)] | Analyzer12 | 13 ▬ | P1.12 | P2.12 | ▬ 14 | Analyzer28 | Link#0 Clock Fail [LK0CLK_FAIL] |
| Link0 Data bit 11 [Link0_in(14)] | Analyzer11 | 15 ▬ | P1.11 | P2.11 | ▬ 16 | Analyzer27 | Link#0 SYNC protocol OK [LK0_SYNC_OK] and SYNC protocol OK after synchronization. |
| Link0 Data bit 10 [Link0_in(13)] | Analyzer10 | 17 ▬ | P1.10 | P2.10 | ▬ 18 | Analyzer26 | Link#0 Frame Synchronization OK |
| Link0 Data bit 9 [Link0_in(12)] | Analyzer9 | 19 ▬ | P1.09 | P2.09 | ▬ 20 | Analyzer25 | Link#0 Clock Internal DLL Locked signal [LK0CLK_DLLI_LOCKED] |
| Link0 Data bit 8 [Link0_in(9)] | Analyzer8 | 21 ▬ | P1.08 | P2.08 | ▬ 22 | Analyzer24 | Link#0 Clock External DLL enable signal from Clock Controller [nIDLL_EN] |
| Link0 Data bit 7 [Link0_in(8)] | Analyzer7 | 23 ▬ | P1.07 | P2.07 | ▬ 24 | Analyzer23 | Global Clock FAIL signal from Clock Controller [GCLK_FAIL] |
| Link0 Data bit 6 [Link0_in(7)] | Analyzer6 | 25 ▬ | P1.06 | P2.06 | ▬ 26 | Analyzer22 | Link#0 Walking 1 pattern OK [LK0_W1pattern_OK] |
| Link0 Data bit 5 [Link0_in(6)] | Analyzer5 | 27 ▬ | P1.05 | P2.05 | ▬ 28 | Analyzer21 | Link#0 Walking 0 pattern OK [LK0_W0pattern_OK] |
| Link0 Data bit 4 [Link0_in(4)] | Analyzer4 | 29 ▬ | P1.04 | P2.04 | ▬ 30 | Analyzer20 | Link0 Data bit 20 [Link0_in(26)] |
| Link0 Data bit 3 [Link0_in(3)] | Analyzer3 | 31 ▬ | P1.03 | P2.03 | ▬ 32 | Analyzer19 | Link0 Data bit 19 [Link0_in(25)] |
| Link0 Data bit 2 [Link0_in(2)] | Analyzer2 | 33 ▬ | P1.02 | P2.02 | ▬ 34 | Analyzer18 | Link0 Data bit 18 [Link0_in(24)] |
| Link0 Data bit 1 [Link0_in(1)] | Analyzer1 | 35 ▬ | P1.01 | P2.01 | ▬ 36 | Analyzer17 | Link0 Data bit 17 [Link0_in(22)] |
| Link0 Data bit 0 [Link0_in(0)] | Analyzer0 | 37 ▬ | P1.00 | P2.00 | ▬ 38 | Analyzer16 | Link0 Data bit 16 [Link0_in(21)] |

Table 4.30, HP Logic Analyzer connector J7 preset configuration 0 (default, 21 bit link monitoring)

| Notes [schematic name of monitored signal] | Schematic name | Pin # | Pin name | Pin name | Pin # | Schematic name | Notes [schematic name of monitored signal] |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | N.C. | 1 ▬ | +5VDC | SCL | ▬ 2 | N.C. |  |
|  | GND | 3 ▬ | GND | SDA | ▬ 4 | N.C. |  |
|  | N.C. | 5 ▬ | CLK1 | CLK2 | ▬ 6 | N.C. |  |
| Link0 Data bit 15 [Link0_in(15)] | Analyzer15 | 7 ▬ | P1.15 | P2.15 | ▬ 8 | Analyzer31 | Link#0 clock [RXCLK0] |
| Link0 Data bit 14 [Link0_in(14)] | Analyzer14 | 9 ▬ | P1.14 | P2.14 | ▬ 10 | Analyzer30 | Global clock [CLK] |
| Link0 Data bit 13 [Link0_in(13)] | Analyzer13 | 11 ▬ | P1.13 | P2.13 | ▬ 12 | Analyzer29 | Global SYNC [GSYNC] |
| Link0 Data bit 12 [Link0_in(12)] | Analyzer12 | 13 ▬ | P1.12 | P2.12 | ▬ 14 | Analyzer28 | Link#0 Clock Fail [LK0CLK_FAIL] |
| Link0 Data bit 11 [Link0_in(11)] | Analyzer11 | 15 ▬ | P1.11 | P2.11 | ▬ 16 | Analyzer27 | Link0 Data bit 27 [Link0_in(27)] |
| Link0 Data bit 10 [Link0_in(10)] | Analyzer10 | 17 ▬ | P1.10 | P2.10 | ▬ 18 | Analyzer26 | Link0 Data bit 26 [Link0_in(26)] |
| Link0 Data bit 9 [Link0_in(9)] | Analyzer9 | 19 ▬ | P1.09 | P2.09 | ▬ 20 | Analyzer25 | Link0 Data bit 25 [Link0_in(25)] |
| Link0 Data bit 8 [Link0_in(8)] | Analyzer8 | 21 ▬ | P1.08 | P2.08 | ▬ 22 | Analyzer24 | Link0 Data bit 24 [Link0_in(24)] |
| Link0 Data bit 7 [Link0_in(7)] | Analyzer7 | 23 ▬ | P1.07 | P2.07 | ▬ 24 | Analyzer23 | Link0 Data bit 23 [Link0_in(23)] |
| Link0 Data bit 6 [Link0_in(6)] | Analyzer6 | 25 ▬ | P1.06 | P2.06 | ▬ 26 | Analyzer22 | Link0 Data bit 22 [Link0_in(22)] |
| Link0 Data bit 5 [Link0_in(5)] | Analyzer5 | 27 ▬ | P1.05 | P2.05 | ▬ 28 | Analyzer21 | Link0 Data bit 21 [Link0_in(21)] |
| Link0 Data bit 4 [Link0_in(4)] | Analyzer4 | 29 ▬ | P1.04 | P2.04 | ▬ 30 | Analyzer20 | Link0 Data bit 20 [Link0_in(20)] |
| Link0 Data bit 3 [Link0_in(3)] | Analyzer3 | 31 ▬ | P1.03 | P2.03 | ▬ 32 | Analyzer19 | Link0 Data bit 19 [Link0_in(19)] |
| Link0 Data bit 2 [Link0_in(2)] | Analyzer2 | 33 ▬ | P1.02 | P2.02 | ▬ 34 | Analyzer18 | Link0 Data bit 18 [Link0_in(18)] |
| Link0 Data bit 1 [Link0_in(1)] | Analyzer1 | 35 ▬ | P1.01 | P2.01 | ▬ 36 | Analyzer17 | Link0 Data bit 17 [Link0_in(17)] |
| Link0 Data bit 0 [Link0_in(0)] | Analyzer0 | 37 ▬ | P1.00 | P2.00 | ▬ 38 | Analyzer16 | Link0 Data bit 16 [Link0_in(16)] |

Table 4.31, HP Logic Analyzer connector J7 preset configuration 1 (28 bit link monitoring)

## Power Supply and safety features

The Mixer Boards are powered through the backplane connectors (see Paragraph 10, page 110 for connectors pinout). The backplane is powered by a Vicor [Ref. 39] Mini PFC power supply using three 80 Amperes modules in parallel for a total of 240 Amperes @ +3.3Volt. The backplane is also connected to a +5V “brick” style supply to provide power to the subrack controller. A sketch of the mixer backplane is provided in Figure 4.5, detailed backplane description is available in separate documents [Ref. 8]. The two mixer board backplane connectors provide a total of 25 3.3Volt pins and 175 ground pins. The Mixer board 3.3Volt input is protected from both over-current and over-voltage with a 10 Amperes fuse and a 1N5908 zener transient voltage suppressor [Ref. 35].

Xilinx Virtex FPGAs need to be powered with two voltages, 3.3Volt (I/Os) and 2.5Volt (core). The 2.5Volt is generated from the 3.3Volt with a Micrel 39500 low dropout 5 Amperes regulator [Ref. 32]. The input of the Micrel regulator is protected from over-current with a 4 Amperes fuse.

# Mixer Board Configuration

The Mixer Board uses a total of 17 FPGAs, 7 Xilinx Spartan XCS40XL and 10 Xilinx Virtex XCV50. The XCS40XL has 330,647 configuration bits (PROM size: 330,696), the XCV50 has 559,232 configuration bits. One of the Spartan devices is used as the Board Controller and a Xilinx XC18V01 In-System-Programmable PROM automatically configures it at power-up. This PROM has a capacity of 1,048,576 bits and can be reprogrammed using JTAG. [Ref.40].

The top row of the LVDS input connector (see Table 4.2) allows access from the front panel to the board controller JTAG chain. This permits the reprogramming of the board controller EEPROM without removing the board from the mixer subrack

After being configured (at power up) the board controller is ready to handle the configuration data for the remaining 16 FPGAs. This data is fed to the board controller through the A16:D8 general-purpose backplane bus [Paragraph 4.5] by the subrack controller located in slot 1 or alternatively by mean of one of the board JTAG ports.

(A note of caution: The download of a wrong configuration file to a device can cause not only a system malfunction but also irreversible hardware damage.

## Configuration through JTAG

As was already mentioned the board controller FPGA firmware can be changed by reprogramming its configuration EEPROM through one of the two JTAG chains (see paragraph 4.7). The remaining sixteen FPGAs can be programmed through the second JTAG chain. But contrary to the board controller, which is reprogrammed at power-up with the configuration data stored in the EEPROM, the other FPGAs will need to be reconfigure after each power-up.

The JTAG configuration method has been extensively used during the initial mixer board testing and debugging and has proved itself to be a very valuable feature.

The software used to configure/program devices through the JTAG ports is the "Xilinx JTAG Programmer" [Ref. 40]. The software Help Menu provides thorough instructions for configuration and program operations. In order to perform configuration correctly the devices part of a JTAG chain needs to be specified in the right order (refer to paragraph 4.7) and each device definition should point to its "bit" file. The JTAG chain information is usually stored in a Chain Description File (extension "cdf").

The hardware needed for this procedure, beside a PC is one of the Xilinx JTAG cables:

Parallel cable, connects to any PC using the standard IEEE-1284 compliant parallel port.

MultiLINX cable, takes advantage of the USB port found on newer PCs and the serial port (RS232) on most PCs & work stations.

It should be noted that the files for JTAG configuration are different than those used for configuration through the A16:D8 backplane bus using the Subrack Controller. The files need to be generated with the configuration option set to JTAG in the "Xilinx Design Manager tool".

## Configuration through the subrack general purpose bus.

The Subrack Controller [Paragraph 14.1] has the FPGAs configuration information stored in a removable CompactFlash™ memory card [Paragraph 14.2]. The CompactFlash™ can be easily inserted/removed from the subrack controller front panel. This memory card allows the storage of multiple configuration sets for the FPGAs of the 20 Mixer Boards inside the Mixer System Subrack. Having more than one set of FPGAs configurations available allow for more reliable/efficient FPGAs firmware updates with the ability to return almost immediately to the previously used firmware version if the new one doesn't perform as expected.

| Device # | Device Type | Schematic device#, device name | Mixer#1 files | Mixer#2 files | Mixer#3 files | Mixer#4 files |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | Spartan XL | U2, DFE1 YP (Outlink 5). | 0200_PC.bin | 0300_PC.bin | 0400_PC.bin | 0500_PC.bin |
| 1 | Spartan XL | U1, DFE1 RB (Outlink 6). | 0201_PC.bin | 0301_PC.bin | 0401_PC.bin | 0501_PC.bin |
| 2 | Spartan XL | U10, DFE1 OG (Outlink 4). | 0202_PC.bin | 0302_PC.bin | 0402_PC.bin | 0502_PC.bin |
| 3 | Spartan XL | U11, DFE0 RB (Outlink 3). | 0203_PC.bin | 0303_PC.bin | 0403_PC.bin | 0503_PC.bin |
| 4 | Spartan XL | U19, DFE0 OG (Outlink 1). | 0204_PC.bin | 0304_PC.bin | 0404_PC.bin | 0504_PC.bin |
| 5 | Spartan XL | U18, DFE0 YP (Outlink 2). | 0205_PC.bin | 0305_PC.bin | 0405_PC.bin | 0505_PC.bin |
| 6 | Virtex | U31, LINK_IN 13-15. | 0206_PC.bin | 0306_PC.bin | 0406_PC.bin | 0506_PC.bin |
| 7 | Virtex | U45, LINK_IN 4-6. | 0207_PC.bin | 0307_PC.bin | 0407_PC.bin | 0507_PC.bin |
| 8 | Virtex | U46, LINK_IN 1-3. | 0208_PC.bin | 0308_PC.bin | 0408_PC.bin | 0508_PC.bin |
| 9 | Virtex | U32, LINK_IN 10-12. | 0209_PC.bin | 0309_PC.bin | 0409_PC.bin | 0509_PC.bin |
| 10 | Virtex | U47, LINK_IN 0. | 020A_PC.bin | 030A_PC.bin | 040A_PC.bin | 050A_PC.bin |
| 11 | Virtex | U48, Backplane Left Driver. | 020B_PC.bin | 030B_PC.bin | 040B_PC.bin | 050B_PC.bin |
| 12 | Virtex | U33, LINK_IN 7-9. | 020C_PC.bin | 030C_PC.bin | 040C_PC.bin | 050C_PC.bin |
| 13 | Virtex | U12, Backplane DFE0 receiver. | 020D_PC.bin | 030D_PC.bin | 040D_PC.bin | 050D_PC.bin |
| 14 | Virtex | U5, Backplane DFE1 receiver. | 020E_PC.bin | 030E_PC.bin | 040E_PC.bin | 050E_PC.bin |
| 15 | Virtex | U6, Backplane Right Driver. | 020F_PC.bin | 030F_PC.bin | 040F_PC.bin | 050F_PC.bin |

Table 5.1, Configuration Files denomination.

| Mixer# | Subrack slots |
| --- | --- |
| 1 | 02, 06, 10, 14, 18 |
| 2 | 03, 07, 11, 15, 19 |
| 3 | 04, 08, 12, 16, 20 |
| 4 | 05, 09, 13, 17, 21 |

Table 5.2, Mixer# and Subrack slot#.

Table 5.1 lists the sixteen FPGA devices with the names of their configuration files. Each device is configured with one of the four sets of files corresponding to the four boards in a mixer subsystem (Mixer 1, Mixer 2, Mixer 3, Mixer 4). The file naming convention is <FSslot#><Device#>_PC.bin, where "FSslot#" is the slot# in the first mixer subsystem (marked in bold in Table 5.2) and "Device#" is the one reported in Table 5.1. Note that the device numbering scheme in Table 5.1 is different from the one used in the JTAG chain (Table 4.25).

Since the configuration file for a particular device is used in five boards the subrack controller command sequence take advantage of the "Mixer Board # Broadcasting" feature (paragraph 4.5 and Table 4.4). This feature allows for writing configuration data contemporaneously to five boards.

A few steps need to be followed in order to correctly generate the configuration files:

- Bit file generation. 
Virtex devices use the default configuration options, with CCLK as startup-clock. Spartan devices need some more attention. The parallel configuration used for them is called "Express Mode" and a user configuration template must be defined for it using the "Template Manager" utility. The template can be named "Express_Mode" and should contain the following options for the bitgen executable: "-g ExpressMode:Enable -g CRC:Disable". The newly defined "Express_Mode" configuration template should then be selected in the design>option>configuration menu before generating the bit file.

- Bit files conversion to HEX files. 
Bit files need to be converted in HEX files using the Xilinx PROM File Formatter utility. The following options must be used.
PROM File Format: HEX;
Value used to calculate checksum: 00;
Swap bits: ON.

- HEX ASCII files conversion to HEX binary.
Xilinx HEX files are ASCII representation of binary data. They must be converted to binary format. This can be done using the HEX2BIN utility [Ref. 5].

- File naming and copying to CompactFlash.
The last step is to organize the files with the naming convention of Table 5.1 and copy them to the CompactFlash card (see Paragraph 14.2).

In order for the device to be configured, the subrack controller should be provided with files containing the sequence of configuration commands. The content of the two standard command files is reported in Paragraph 14.2.2. A list of available commands is available in Paragraph 14.3.

# Monitoring and Debugging features

## Front Panel LEDs

The front panel accommodates sixteen bicolor LEDs numbered from 0 to 15 and two red LEDs (see

Figure 6.1). The red LEDs are powered by the 3.3 Volt supply and 2.5 Volt on-board regulator. The bicolor LEDs are controlled by the FPGAs and allow monitoring of the state of several signals. The reset push button is used to select the set of signal to be displayed by the LEDs. At power up, the default set is set number twelve. Pushing the reset button (for less then two seconds) allows the user to select the next set. Immediately after the reset button is pushed the LEDs will indicate for about two seconds the selected set of signal that will be displayed. Pressing the reset button for more then two seconds forces the mixer board to reset.

If not specified otherwise, the LED use is as follows: green LED ON if signal is in a logic low state, red LED ON if signal is in a logic high state. Each LED is controlled by it's own state machine which stretches the signal driving the LED to a minimum of 150msec in order to make it visible to the human eye. If a signal is continuously changing both the green and red LEDs will be ON resulting in a yellow color.

Figure 6.1, Front panel LEDs and LEDs monitoring mode

The following tables describe the sixteen available sets of signals (or monitoring modes).

| LED# | Led Use. This set is used to monitor the input links clocks and DLLs. Link clock: Green LED ON if clock present, clock frequency is 45MHz < f < 55MHz and clock DLL is locked. Red LED-ON otherwise. |
| --- | --- |
| 15..0 | Link #15 to Link#0 clock status. |

Table 6.1, LED's set #0 (input links clock and DLLs status).

| LED# | Led Use. This set is used to monitor the SYNC bit (data frame synchronization bit located on the LSb of each LVDS link). The link's own clock is used as timing reference. Green LED ON only if the SYNC bit is present and is respecting the protocol (one and only one high bit every seven clock cycles). Red LED ON otherwise. |
| --- | --- |
| 15..0 | Link #15 to Link#0 sync bit status. |

Table 6.2, LED's set #1 (input links SYNC bit status).

| LED# | Led Use. This set is used to check the presence on the input links of a walking one test pattern. The pattern is specified in Paragraph 11. The link's own clock is used as timing reference. Green LED ON if the walking one pattern is detected, Red LED ON otherwise. |
| --- | --- |
| 15..0 | Link #15 to Link#0 walking one test pattern presence. |

Table 6.2, LED's set #2 (input links Walking 1 test pattern detection).

| LED# | Led Use. This set is used to check the presence on the input links of a walking zero test pattern. The pattern is specified in Paragraph 11. The link's own clock is used as timing reference. Green LED ON if the walking zero pattern is detected, Red LED ON otherwise. |
| --- | --- |
| 15..0 | Link #15 to Link#0 walking zero test pattern presence. |

Table 6.3, LED's set #3 (input links Walking 0 test pattern detection).

| LED# | Led Use. This set is used to monitor the SYNC bit (data frame synchronization bit located on the LSb of each LVDS link) after the synchronization process. The Global Clock is used as timing reference. Green LED ON only if the SYNC bit is present and is respecting the protocol (one and only one high bit every seven clock cycles). Red LED ON otherwise. |
| --- | --- |
| 15..0 | Link #15 to Link#0 sync bit status after synchronization. |

Table 6.2, LED's set #4 (input links SYNC bit status after synchronization).

| LED# | Led Use. This set is used to monitor the synchronization of the input links frames with the global sync. A link data frame is considered synchronized when the SYNC bit is in received in the same frame time slot as the SYNC bit used as timing reference (usually the SYNC received on link#0 of Mixer board #1). Green LED ON if link data frames are synchronized, Red LED ON otherwise. |
| --- | --- |
| 15..0 | Link #15 to Link#0 synchronization status. |

Table 6.4, LED's set #5 (input links frame synchronization status).

| LED# | Link #0 Output links Test Pattern detection. It is used to test the mixer output link when they are sending the test pattern. The test pattern transmission can be enabled through the Output Links Test Mode registers. The output links test pattern is specified in Paragraph 11. A 28 bit type LVDS cable should be used to loop-back one of the output links to the link#0 input link. Green LED ON if the pattern is detected, Red LED ON otherwise. |
| --- | --- |
| 0 | pattern detection. |
| 1..15 | not used, always OFF. |

Table 6.5, LED's set #6 (Output links test pattern detection).

| LED# | Input links control bits stream monitoring. Each LED is driven by the sequence of seven data bits received on a particular link. If a LED is red it means that the control bits on that link are always high ('1'), if the LED is green the control bits are always low ('0'). If the LED is orange it means that on that link some control bits are high and same are low or that at least one control bit is changing status. By default all the control bits are monitored, but a mask can be set in the "Monitoring Mode 7 Mask registers" (See 7.1.12) to monitor only a subset of control bits. |
| --- | --- |
| 15..0 | Link #15 to Link #0 control bits stream. |

Table 6.6, LED's set #7 (Input links control bits stream monitoring).

| LED# | Mixer Board local bus monitoring. This set is used to monitor the local bus data, address and control signals. When FPGAs device access operations are enabled (see Paragraph for an example) this monitoring mode can be used to view the content of FPGA's internal registers directly on the front panel LEDs. This is because when device access is enabled the local bus is driven with the content of FPGAs internal registers. |
| --- | --- |
| 0 | Local Data Bus bit 0 (FDAT0). |
| 1 | Local Data Bus bit 1 (FDAT1). |
| 2 | Local Data Bus bit 2 (FDAT2). |
| 3 | Local Data Bus bit 3 (FDAT3). |
| 4 | Local Data Bus bit 4 (FDAT4). |
| 5 | Local Data Bus bit 5 (FDAT5). |
| 6 | Local Data Bus bit 6 (FDAT6). |
| 7 | Local Data Bus bit 7 (FDAT7). |
| 8 | Local Data Bus read/write (/WRITE). |
| 9 | Local Bus Address Strobe (ASTRB) and FPGAs /INIT. |
| 10 | Local Bus Data Strobe (DSTRB). |
| 11 | FPGAs /PROGRAM (/PROGRAM). |
| 12 | FPGAs Configuration Clock (CONFIGCLK), green LED ON if clock is present, red LED ON if is absent. |
| 13 | Local Bus Transceiver enable (/CONFIGDAT_EN). |
| 14 | Local Bus Transceiver direction (/CONFIGDAT_DIR). '1' FPGAs to Board Controller, '0' Board Controller to FPGAs. |
| 15 | FPGA Global Clock (FPGACLK10), green LED ON if clock is present, red LED ON if is absent. |

Table 6.7, LED's set #8 (Mixer Board local bus monitoring).

| LED# | Backplane serial bus and A16:D8 control signals monitoring. This set is used to monitor the A16:D8 general purpose bus control signals and the slow monitoring serial bus part of the backplane interfaces between the Mixer Board and the subrack controller. |
| --- | --- |
| 0 | SYSCLOCK (green LED ON if clock is present, red LED if clock is absent). |
| 1 | Address STRoBe (AS). |
| 2 | WRITE (WRITE). |
| 3 | Data Transfer ACKnoledge (/DTACK). |
| 4 | Bus ERRor (/BERR). |
| 5 | SYSRESET (SYSRST). |
| 6 | Transceivers enable (/VDAT_EN). |
| 7 | Transceiver direction (VDAT_DIR). |
| 8 | Serial Link Reset (STAT_RST). |
| 9 | Serial Link Clock (STAT_CLK), green LED ON if clock is present, red LED if clock absent. |
| 10 | Serial Link Data (STAT_DAT[n]). |
| 11 | Broadcast addressing. |
| 12 | Not Standard Mode (from Slow Monitoring register). |
| 13 | Input Links Error (from Slow Monitoring register) |
| 14 | Global Clock/SYNC Error (from Board Status/Control register) |
| 15 | Global Clock/SYNC Error history (from Board Status/Control register) |

Table 6.8, LED's set #9 (Backplane serial bus and A16:D8 bus control signals monitoring).

| LED# | Led Use. This set is used to monitor the backplane address bus part of the A16:D8 general purpose bus interface between the Mixer Board and the subrack controller. |
| --- | --- |
| 0..15 | Address bit 0 (BADDR0) to Address bit 15 (BADDR15). |

Table 6.5, LED's set #10 (Backplane A16:D8 general purpose bus address signals monitoring).

| LED# | This set is used to monitor the backplane data and geographical address signals part of the A16:D8 general purpose bus interface between the Mixer Board and the subrack controller. |
| --- | --- |
| 0 | Data bit 0 (BDAT0). |
| 1 | Data bit 1 (BDAT1). |
| 2 | Data bit 2 (BDAT2). |
| 3 | Data bit 3 (BDAT3). |
| 4 | Data bit 4 (BDAT4). |
| 5 | Data bit 5 (BDAT5). |
| 6 | Data bit 6 (BDAT6). |
| 7 | Data bit 7 (BDAT7). |
| 8 | Slot Address bit 0 (MOD_ID0). |
| 9 | Slot Address bit 1 (MOD_ID1). |
| 10 | Slot Address bit 2 (MOD_ID2). |
| 11 | Slot Address bit 3 (MOD_ID3). |
| 12 | Slot Address bit 4 (MOD_ID4). |
| 13 | Not used, always OFF. |
| 14 | Not used, always OFF. |
| 15 | Not used, always OFF. |

Table 6.5, LED's set #11 (A16:D8 general purpose bus data and slot address signals monitoring).

| LED# | This set is used to verify the configuration of 16 of the 17 FPGAs of a Mixer Board. The only FPGA not considered is the Board Controller which is automatically configured at power-up by an EPROM. Green: FPGA configured correctly. Red: FPGA not configured. The name in parenthesis is the one used on the board electrical schematic. |
| --- | --- |
| 0 | Configuration Done BE DFE1 Yellow-Purple FPGA (DONE11). |
| 1 | Configuration Done BE DFE1 Red-Blue FPGA (DONE12). |
| 2 | Configuration Done BE DFE1 Orange-Green FPGA (DONE13). |
| 3 | Configuration Done BE DFE0 Red-Blue FPGA (DONE14). |
| 4 | Configuration Done BE DFE0 Orange-Green FPGA (DONE15). |
| 5 | Configuration Done BE DFE0 Yellow-Purple FPGA (DONE16). |
| 6 | Configuration Done FE LinkIn13..15 FPGA (DONE1). |
| 7 | Configuration Done FE LinkIn4..6 FPGA (DONE2). |
| 8 | Configuration Done FE LinkIn1..3 FPGA (DONE3). |
| 9 | Configuration Done FE LinkIn10..12 FPGA (DONE4). |
| 10 | Configuration Done FE LinkIn0 FPGA (DONE5). |
| 11 | Configuration Done Backplane Left Driver FPGA (DONE6). |
| 12 | Configuration Done FE LinkIn7..9 FPGA (DONE7). |
| 13 | Configuration Done Backplane DFE0 Receiver FPGA (DONE8). |
| 14 | Configuration Done Backplane DFE1 Receiver FPGA (DONE9). |
| 15 | Configuration Done Backplane Right Driver FPGA (DONE10). |

Table 6.6, LED's set #12 (Default mode, FPGA configuration status).

| LED# | Output Links Test Mode Enable status. |
| --- | --- |
| 0 | DFE 0 Green Link (00) status. |
| 1 | DFE 0 Green Link (01) status. |
| 2 | DFE 0 Orange Link (02) status. |
| 3 | DFE 0 Purple Link (03) status. |
| 4 | DFE 0 Yellow Link (04) status. |
| 5 | DFE 0 Blue Link (05) status. |
| 6 | DFE 0 Red Link (06) status. |
| 7 | DFE 0 Red Link (07) status. |
| 8 | DFE 1 Green Link (10) status. |
| 9 | DFE 1 Green Link (11) status. |
| 10 | DFE 1 Orange Link (12) status. |
| 11 | DFE 1 Purple Link (13) status. |
| 12 | DFE 1 Yellow Link (14) status. |
| 13 | DFE 1 Blue Link (15) status. |
| 14 | DFE 1 Red Link (16) status. |
| 15 | DFE 1 Red Link (17) status. |

Table 6.7, LED's set #13 (Output Links Test Mode Enable status).

| LED# | Input Links Error Status. This set is used to monitor the input links status using the same signals driving Input Links Error Status registers (0x05, 0x06). |
| --- | --- |
| 15..0 | Status of the input links #15 (bit 15) to #0 (bit 0). A high value ('1', red LED ON) indicates that the corresponding input link has one of the following critical errors: Link clock: missing or out of frequency range (45MHZ to 55MHz) or Delay Locked Loop not locked; Link frame marker (SYNC) before synchronization: missing or not respecting the protocol (one and only one high bit every seven clock cycles); Link frame marker (SYNC) after synchronization: missing or not respecting the protocol (one and only one high bit every seven clock cycles); Link frame synchronization: the frames are not synchronized with those of the reference link (usually link#0 on the first board (master) in the mixer subsystem (group of four boards handling the data from one supersector)). |

Table 6.7, LED's set #14 .(Input Links Error Status).

| LED# | Led Test. This set is used to check that all the LEDs are functioning. |
| --- | --- |
| 15..0 | Both Green and Red LEDs are always ON (Orange light). |

Table 6.7, LED's set #15 (LED Test).

# Appendix A – Devices registers

The board controller internal registers allow for most of the user controls needed during normal system operations. Beside the board controller there are sixteen FPGAs on a mixer board and each one has internal registers. These registers allow access to advanced features generally used for diagnostic purposes during system debugging, testing and commissioning. These features can also be utilized periodically to test system operations or in the event of a malfunction.

## FrontEnd Devices

Table 7.1 lists the internal registers of the six front-end FPGAs. The address specified in the first column refers to the FPGA internal address and is the one to be used in the Device Access Address register. Please refer to Paragraph 4.5.12 for more information on the Device Access Structure. The table is followed by a description of each of the registers.

| Register address | Register name and use. | IN0 [Dev# 1010b] | IN1..3 [Dev# 1000b] | IN4..6 [Dev# 0111b] | IN7..9 [Dev# 1100b] | IN10..12 [Dev# 1001b] | IN13..15 [Dev# 0110b] |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0x00 | Device Firmware | X | X | X | X | X | X |
| 0x01 | Link pointer | X | -- | -- | -- | -- | -- |
| 0x02..0x0F | -- | -- | -- | -- | -- | -- | -- |
| 0x10 | Link Status A (Read-Only) | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x11 | Link Status B (Read-Only) | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x12 | Link Control (Read/Write) | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x13 | Frame Sync Status (Read-Only) | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x14 | Frame Sync Status History (Read-Only) | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x15 | Monitoring Mode 7 Mask | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x16 | Link Control Bits Status | Link#0 | Link#1 | Link#4 | Link#7 | Link#10 | Link#13 |
| 0x17..0x1F | -- | -- | -- | -- | -- | -- | -- |
| 0x20 | Link Status A (ReadOnly) | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x21 | Link Status B (ReadOnly) | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x22 | Link Control (Read/Write) | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x23 | Frame Sync Status (Read-Only) | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x24 | Frame Sync Status History (Read-Only) | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x25 | Monitoring Mode 7 Mask | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x26 | Link Control Bits Status | -- | Link#2 | Link#5 | Link#8 | Link#11 | Link#14 |
| 0x27..0x2F | -- | -- | -- | -- | -- | -- | -- |
| 0x30 | Link Status A (Read-Only) | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x31 | Link Status B (Read-Only) | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x32 | Link Control (Read/Write) | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x33 | Frame Sync Status (Read-Only) | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x34 | Frame Sync Status History (Read-Only) | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x35 | Monitoring Mode 7 Mask | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x36 | Link Control Bits Status | -- | Link#3 | Link#6 | Link#9 | Link#12 | Link#15 |
| 0x37..0x3F | -- | -- | -- | -- | -- | -- | -- |
| 0x40 | Control bits masking | Link#0 | -- | -- | -- | -- | -- |
| 0x41 | Control bits masking | Link#1 | -- | -- | -- | -- | -- |
| 0x42 | Control bits masking | Link#2 | -- | -- | -- | -- | -- |
| 0x43 | Control bits masking | Link#3 | -- | -- | -- | -- | -- |
| 0x44 | Control bits masking | Link#4 | -- | -- | -- | -- | -- |
| 0x45 | Control bits masking | Link#5 | -- | -- | -- | -- | -- |
| 0x46 | Control bits masking | Link#6 | -- | -- | -- | -- | -- |
| 0x47 | Control bits masking | Link#7 | -- | -- | -- | -- | -- |
| 0x48 | Control bits masking | Link#8 | -- | -- | -- | -- | -- |
| 0x49 | Control bits masking | Link#9 | -- | -- | -- | -- | -- |
| 0x4A | Control bits masking | Link#10 | -- | -- | -- | -- | -- |
| 0x4B | Control bits masking | Link#11 | -- | -- | -- | -- | -- |
| 0x4C | Control bits masking | Link#12 | -- | -- | -- | -- | -- |
| 0x4D | Control bits masking | Link#13 | -- | -- | -- | -- | -- |
| 0x4E | Control bits masking | Link#14 | -- | -- | -- | -- | -- |
| 0x4F | Control bits masking | Link#15 | -- | -- | -- | -- | -- |
| 0x50 | Input Links Control bits status at Link0 FPGA | Link#15..0 | -- | -- | -- | -- | -- |
| 0x51 | EC bits status | X | -- | -- | -- | -- | -- |
| 0x52 | ECS bits status | X | -- | -- | -- | -- | -- |
| 0x53..0xFF | -- | -- | -- | -- | -- | -- | -- |

Table 7.1, Front-End devices registers.

### Device Firmware Register

This register contains information about the FPGA/device accessed. It allows verifying which device is being accessed.

Figure 7.1, Device Firmware register.

### Link pointer register

Allows selecting which link is to be monitored by some of the diagnostic. The diagnostic information can be read back through FPGA's internal registers. The content of these registers depends on the link pointed to by the "Link Pointer register". The four bits used as link pointer represent the link# in hexadecimal.

Figure 7.2, Link Pointer register

Currently only the "Input Links Control bits status at IN0 FPGA" register needs the Link pointer register.

### Input Link Status registers

Figure 7.3, Input Link Status register.

### Input Link Control register

Figure 7.4, Input Link Control register

Figure 7.5, Data synchronization and link controls.

### Frame Sync Status register

The frame synchronization register data is used to determine the link SYNC (link frame marker) position relative to the global SYNC. Its content is generated by sampling with the global SYNC signal the content of an 8bit long shift register fed by the link SYNC. When the data frames on a link are synchronized to the global SYNC all of the bits but the least and most significative will readback “0” (see Figure 7.7).

Figure 7.6, Frame Synchronization Status register.

Figure 7.7, Frame Synchronization Status register content.

### Frame Sync Status History register

The Frame Sync Status History register is used to keep track of the changes in the Frame Sync Status register. The register content is zero at power up or reset (or with the "reset history information" from Input Link Control register) and each of is bit is set and remain set to '1' if the corresponding bit in the Frame Sync Status register is '1'.

Figure 7.8, Frame Synchronization Status History register.

### Input Link Control Bits Mask register

Each input link is preset to receive one control bit at each time slot embedded in the 7-time slot data stream, for a total of 7 control bits per link. The control bits from every link are sent to one FPGA (the Link#0 FPGA) where, at each time slot, they are all ORed and XORed to generate the Embedded Command (EC) and the Embedded Command Status (ECS) bit. The EC and ECS bits are then sent to the backend FPGAs to be embedded in some of the output data streams.

If any of the control bits are not sent by the front end electronics (AFEs) to the mixer, the missing control bits need to be masked on the Mixer boards in order to perform the OR and XOR operation only on the valid control bits. This masking is done in the Link#0 FPGA before the OR and XOR operation are performed. To allow this, there are 16 "input link control bits mask registers" for each input link on a mixer board. If any control bit needs to be masked, the corresponding bit in the masking register should be set to '0'. The default content of each of these registers is 0x01 for link#0 and 0xFF for all the other links. The reason for having all the control bits masked on input link#0 is that the data mapping done by the AFEs driving link#0 doesn't comply with the mixer design specification so the control bits aren't where the mixer would expect them.

Figure 7.9, Input Link Control Bits Mask register.

### Input Link Control Bits Status registers

Allows verifying of the presence of control bits on each of the sixteen input links. There is one of these registers for each input link.

The registers content reflects the control bits received on each link and is not affected by any control bits mask selection made in the "Input Link Control Bits Mask register".

Figure 7.10, Input Link Control Bits Status register

### Input Link Control Bits Status at Link#0 FPGA register

Allows verifying of the presence of control bits from each of the sixteen input links at the Link#0 FPGA, which is the place where the control bits are combined to generate the Embedded Command and Embedded Command Status bits for the output data stream.

Only one link at a time can be monitored. The link to be monitored is selected in the "Link Pointer register" inside the IN0 FPGA (device# 0x0A). The register content reflects the control bits received on each link and is not affected by any control bits mask selection made in the "Input Link Control Bits Mask register". The register is NOT reset when the monitored link is changed. Because of this, after a link change and when the latching option (bit#0) is used there is the need to disable and re-enable it in order for the register to show the correct information.

This register will be probably removed in future firmware upgrades.

Figure 7.11, Input Link Control Bits Status register

### Embedded Command Bits status register

Allows verifying of the presence of the Embedded Command bits generated ORing the control bits received from the 16 input links.

Figure 7.12, Embedded Command Bits Status Register.

### Embedded Command Status Bits status register

Allows verifying of the presence of the Embedded Command Status bits generated XORing the control bits received from the 16 input links.

Figure 7.13, Embedded Command Status Bits Status Register.

### Monitoring Mode 7 Mask register

Each input link is preset to receive one control bit at each time slot embedded in the 7-time slot data stream, for a total of 7 control bits per link. LED monitoring mode 7 (see Paragraph 6.1) allows seeing on the front panel LEDs the presence of the control bits data stream. The Monitoring Mode 7 Mask register allows individual masking on any input link for any set of control bits in order to have monitoring mode 7 shows the presence of a desidered control bits subset. There are 16 "input link control bits mask registers", one for each input link on a mixer board. The default content of each of these registers is 0xFF. If any control bit needs to be masked, the corresponding bit in the masking register should be set to '0'.

Figure 7.14, Monitoring Mode 7 Mask register.

## Backplane Devices

Partially Implemented

Grayed blocks are not implemented.

| Register address | Register name and use. | DFE0_RX [Dev# 1101b] | DFE1_RX [Dev# 1110b] | LEFT_DRV [Dev# 1011b] | RIGHT_DRV [Dev# 1111b] |
| --- | --- | --- | --- | --- | --- |
| 0x00 | Device Firmware | X | X | X | X |
| 0x01 | -- | -- | -- | -- |  |
| 0x02 | Device Control | X | X | X | X |
| 0x03..0x6F | -- | -- | -- | -- | -- |
| 0x70 | Clock DLL Error (Read-Only) | -- | -- | -- | X |
| 0x71 | Clock Frequency Error (Read-Only) | -- | -- | -- | X |
| 0x72 | SYNC Error (Read Only) | -- | -- | -- | X |
| 0x73 | Clock/SYNC Select Status (Read Only) | -- | -- | -- | X |
| 0x74..0x7F | -- | -- | -- | -- | -- |
| 0x80 | Backplane Driver Status (Read-Only) | -- | -- | X | X |
| 0x81 | Backplane Driver Control (Read/Write) | -- | -- | X | X |
| 0x82..0x8F | -- | -- | -- | -- | -- |
| 0x90 | Backplane Receiver Status (Read-Only) | X | X | -- | -- |
| 0x91 | Backplane Receiver Control (Read/Write) | X | X | -- | -- |
| 0x92..0xFF | -- | -- | -- | -- | -- |

Table 7.2, Backplane Devices registers.

### Device Firmware Register

See paragraph 7.1.1.

### Device Control register

Figure 7.15, Device Control register

### Clock DLL Error register

Figure 7.16, Clock DLL Error register.

### Clock Frequency Error register

Figure 7.17, Clock Frequency Error register.

### SYNC Error register

Figure 7.18, SYNC Error register

### Clock/SYNC Select Status register

Figure 7.19, Clock/SYNC Select Status register

### Backplane Driver Status register

NOT IMPLEMENTED

### Backplane Driver Control register

NOT IMPLEMENTED

### Backplane Receiver Status register

NOT IMPLEMENTED

### Backplane Receiver Control register

NOT IMPLEMENTED

## BackEnd Devices

Partially implemented, grayed blocks are not implemented.

| Register address | Register name and use. | DFE0_GO [Dev# 0100b] | DFE0_YP [Dev# 0101b] | DFE0_BR [Dev# 0011b] | DFE1_GO [Dev# 0010b] | DFE1_YP [Dev# 0000b] | DFE1_BR [Dev# 0001b] |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0x00 | Device Firmware | X | X | X | X | X | X |
| 0x01 | -- | -- | -- | -- | -- | -- | -- |
| 0x02 | Device Control | X | X | X | X | X | X |
| 0x03..0x0F | -- | -- | -- | -- | -- | -- | -- |
| 0x10..0x9F | -- | -- | -- | -- | -- | -- | -- |
| 0xA0 | Link Status | Green (00, 01) | Yellow (04) | Blue (05) | Green (10, 11) | Yellow (14) | Blue (15) |
| 0xA1 | Link Control | Green (00, 01) | Yellow (04) | Blue (05) | Green (10, 11) | Yellow (14) | Blue (15) |
| 0xA2 | Embedded Command Bits mask | -- | -- | X | -- | -- | X |
| 0xA3..0xAC | -- | -- | -- | -- | -- | -- | -- |
| 0xAD | Link FIFO Memory Pointer | Green (00, 01) | Yellow (04) | Blue (05) | Green (10, 11) | Yellow (14) | Blue (15) |
| 0xAE | Link FIFO Control | Green (00, 01) | Yellow (04) | Blue (05) | Green (10, 11) | Yellow (14) | Blue (15) |
| 0xAF | Link FIFO Access | Green (00, 01) | Yellow (04) | Blue (05) | Green (10, 11) | Yellow (14) | Blue (15) |
| 0xB0 | Link Status | Orange (02) | Purple (03) | Red (06, 07) | Orange (12) | Purple (13) | Red (16, 17) |
| 0xB1 | Link Control | Orange (02) | Purple (03) | Red (06, 07) | Orange (12) | Purple (13) | Red (16, 17) |
| 0xB2 | Embedded Command Bits mask | X | -- | -- | X | -- | -- |
| 0xB3..0xBC | -- | -- | -- | -- | -- | -- | -- |
| 0xBD | Link FIFO Memory Pointer | Orange (02) | Purple (03) | Red (06, 07) | Orange (12) | Purple (13) | Red (16, 17) |
| 0xBE | Link FIFO Control | Orange (02) | Purple (03) | Red (06, 07) | Orange (12) | Purple (13) | Red (16, 17) |
| 0xBF | Link FIFO Data | Orange (02) | Purple (03) | Red (06, 07) | Orange (12) | Purple (13) | Red (16, 17) |
| 0xC0..0xFF | -- | -- | -- | -- | -- | -- | -- |

Table 7.3, BackEnd Devices registers.

### Device Firmware Register

See paragraph 7.1.1.

### Device Control Register

See paragraph 7.2.2.

### Output Link Status register

NOT IMPLEMENTED

### Output Link Control register

This register allows to shutdown the output link data stream and the output link SYNC bit. Some of the output links are used to transmit the Embedded Command and the Embedded Command Status bits (or control bits). These bits are not affected by the data stream shutdown, if desired they can be masked using the Embedded Command Bits Mask register.

Figure 7.20, Link Control register

### Output Link Embedded Command Bits Mask register

This register allows masking the control bits on the output links. Only 4 output links are carrying control bits, these are the orange (02, 12) and the blue (05, 15) links. The control bits can be masked independently on each of these links. The masking affects both the Embedded Command Bits (ECB) and the Embedded Command Status Bits (ECSB).

Figure 7.21, Embedded Command Bits Mask register.

### Output Link FIFO

Each output link has a 32 bit wide FIFO that can be used to sample the data stream sent to the output link transmitters or to feed the output link transmitters with fake events to test the system downstream.

Figure 7.22, Output Link FIFO

Figure 7.23, Output Link FIFO Access/Control Structure

The FIFO Trigger Control register is used to trigger the output links FIFOs. This register allows selecting the trigger duration from 0 (no trigger) to 15 data frames or a continuous trigger. The trigger duration (even the continuous trigger) will always be an entire number of frames and is automatically synchronized to the global SYNC (frame marker). The trigger operates simultaneously on all the FIFOs on a Mixer Board.

Each individual FIFO can be accessed in Read/Write using the thorough the FIFO Data Access register that connect to one of the 56 byte-wide memory locations of the FIFO. The location accessed is the one pointed by the FIFO Memory Pointer register.

The FIFO can be used to replace events in the output data stream with the FIFO content (transmit mode) or to store events from the output data stream in the FIFO (receive mode). The FIFO can operate in four different “FIFO Event Modes” which are used select the section of the FIFO to be used (event#0, event#1 or both) or to disable the FIFO.

The FIFO is by default in Transmit Mode and in FIFO Event Mode “01”. With these settings, when a trigger is generated (FIFO Trigger Control register), only event#0 will be transmitted for the duration of the trigger. When in transmit mode the FIFO content is set to replace completely the output data stream content including the SYNC and the control bits. The FIFO Control register provides the user with the option to do not disrupt the control bits flow with the FIFO content.

A board reset doesn’t affect the FIFO content.

The FIFO is not accessible when it is receiving a trigger signal.

### Output Link FIFO Memory Pointer register

This register is used to select one of the 56 byte-wide locations of the FIFO. The location pointed by the register is accessible through the "Output Link FIFO Data Access register".

Figure 7.24, Output Link FIFO Memory Pointer register

### Output Link FIFO Control register

This register is used to control the FIFO behavior.

Figure 7.25, Output Link FIFO Control register

| Bit# | Name (Type) | Interpretation |
| --- | --- | --- |
| 7..6 | -- | Not used. |
| 5..4 | FIFO Event Mode Select | The FIFO can operate in four event modes: “00”: FIFO disabled, the trigger is ignored. “01”: FIFO one event deep. Event #0 is used. “10”: FIFO one event deep. Event#1 is used. “11”: FIFO two event deep, both event #0 and #1 are used. The event mode affect both the receive and transmit mode of operation. |
| 3 | -- | Not used |
| 2 | FIFO Trigger | Read Only. Is high when the FIFO is receiving a trigger signal from the board controller (FIFO Trigger Control register). |
| 1 | Control Bits Source Select | Some of the output links are used to transmit control bits together with the data stream. When the FIFO is operating in transmit mode and a trigger is received the content of the FIFO is used on the output link data stream and replace the data bits, the SYNC (frame marker) bit and the control bits. To avoid disrupting the control bit flow the Control Bits Source Select bit can be set high ‘1’. |
| 0 | Receive/Transmit Mode Select | Allow to select if the FIFO has to operate in Transmit (‘0’, default) or in Receive (‘1’) mode. The transmit mode allow to send the FIFO content on the output data stream. The receive mode is used to store portion of the data stream in the FIFO. |

Table 7.4, Output Link FIFO Control Register.

### Output Link FIFO Data Access register

This register allows to access in read/write the 56 byte-wide locations of the Output Link FIFO. When a trigger is active the write access is disabled and the value read is 0xFF.

Figure 7.26, Output Link FIFO Data Access register

# Appendix B – Mixer Board detailed block diagrams

## Mixer Board data flow from LVDS receivers to LVDS transmitters

Figure 8.1 shows a graphical sketch of the interconnections used by the bits of data flowing from the input links LVDS receivers to the output links LVDS transmitters. The PCB Interconnection Matrix block are shows the number of connections between the output of the front-end FPGAs and the back-end FPGAs. Details of the interconnection matrix with the indication of which mixer firmware (Mixer 1 to Mixer 4) is used for a particular connection are reported in Chapter 9.

The link#0 Front-End FPGA performs more functions than the other front-end FPGAs. It receives and forwards to the clock controller (hosted by the backplane right driver FPGA) the link#0 clock. This is the clock used by the clock controller as first choice for the global clock (GCLK). The link#0 FPGA also receive the input links control bits, extracted from the data stream inside the front-end FPGAs, and generate two control bits used in some of the output inks data streams. These output control bits are the Embedded Command bit (ECb)and the Embedded Command Status bit (ECSb).

Each of the back-end FPGAs has two sets of data inputs, one coming from the front-end FPGAs and one coming from the backplane FPGAs. The DFE0 (or plain color) back-end FPGAs receive backplane data only from the DFE0 backplane receiver, the DFE1 (or striped color) back-end FPGAs only from the DFE1 backplane receiver.

Each back-end FPGA produces and sends two unique data streams to the output links LVDS transmitters, but the green and red data streams are duplicated (they feed two LVDS transmitters).

Each of the backplane drivers feed a bus 41 bits wide that connects to the adjacent board to the right or to the left though the backplane. Each of the backplane receivers receives data from both right and left sides over an 82 bits wide bus.

All the FPGAs on the board receive the global clock (GCLK) and global SYNC (GSYNC) from the clock controller. The clock controller has the capability to choose between the backplane clock, the link#0 clock and the local clock.

Figure 8.1, Mixer Board simplified data flow

## Mixer Board Front-End FPGAs

Figure 8.2, Mixer Board Front-End FPGAs

## Mixer Board Back End FPGAs

Figure 8.3, Mixer Board Back-End FPGAs

## Mixer Board Backplane FPGAs

Figure 8.4, Mixer Board Backplane FPGAs

## Control bits (inputs) and command bits (outputs)

Figure 8.5, Command bits generation, timing and denomination.

## Mixer Board Board-Controller

Figure 8.6, Mixer Board Controller

## Mixer System Timing Signals Distribution

Clock and SYNC distribution is critical for the mixer system.

Figure 8.7, Mixer Master clock selection

Figure 8.8, Mixer Slave clock selection

In an ideal situation, each mixer subsystem (group of four boards handling the data belonging to a supersector) will use the same clock/SYNC pair after the input links data synchronization. In order to do this, one of the input links clocks is used as global clock. The link used as clock reference is link#0 of the leftmost board (master) of each mixer subsystem. The master board propagates clock and SYNC to the other three boards (slaves) in the subsystem. The clock controller on a slave board has the choice of three clocks: the backplane clock, the link#0 clock or the local oscillator clock. The clock controller on a master board has only the last two options. The "global sync" is always chosen from the same source of the global clock.

When the mixer system is operating correctly the master boards will be using the link#0 clock and the slave boards will use the backplane clock. In the event a master board doesn't receive a link#0 clock it will switch to the local clock (on-board 53MHz oscillator) for the board "global clock" and switch off the clock backplane distribution to the slave boards.

If a slave board doesn't receive a backplane clock it will switch to the link#0 clock as its first option, and to the local clock (on-board 53MHz oscillator) as its second option.

Figure 8.9, Mixer System Clock Distribution

## Mixer System Data Synchronization

A major issue in the mixer system is synchronizing the input data. Two type of synchronization processes are actually needed:

a) Clock synchronization. It consists of correctly transferring the input data from the input link clock domain to the subsystem clock domain (GCLK).

b) Frame synchronization. It consists of aligning the input data frames to the subsystem frame reference marker (GSYNC).

The mixer firmware doesn't perform any automatic operation to synchronize input data; it provides instead a means to detect synchronization errors and to correct them.

Figure 8.10, Mixer System Data Synchronization

## Mixer Board Frame Synchronization

Frame synchronization signals are part of the mixer design in order to allow for automatic input links frame alignment in a mixer subsystem. This feature is not currently implemented in firmware.

Figure 8.11, Mixer Board Frame Synchronization signals

## Mixer Board spare connections

Figure 8.12, Mixer Board spare connections

The mixer design has some spare connections to allow for fixes and new features. Figure 8.12 shows all the available spare signals. Table 8.1 lists the spare connections currently used.

| FPGA | Signal name | Connected to | Use |
| --- | --- | --- | --- |
| Board Controller | SPRDR[3] | Backplane Right Driver | Connected with a wire to the output enable of a local bus driver (U27pin19). |
| Backplane DFE1 RX | SP1RX[1] | Board Controller | Signal "Backplane DLL Locked" from Backplane DFE1 RX to Backplane Right Driver. |
| Board Controller | SPRDR[2] | Backplane DFE1 RX |  |
| IN0 | SPIN0_[7] | Backplane Right Driver | Signal "Link#0 DLL Locked" from FE IN0 FPGA to Backplane Right Driver. |
| Backplane Right Driver | SPIN0_[6] | IN0 | Signal "Global Clock FAIL" from clock controller to Front-End FPGAs |
| IN0 | FECOM[0] | IN1..3 |  |
| IN0 | FECOM[5] | IN4..6 |  |
| IN0 | FECOM[10] | IN7..9 |  |
| IN0 | FECOM[15] | IN10..12 |  |
| IN0 | FECOM[20] | IN13..15 |  |
| Backplane Right Driver | SPRDR[1] | Board Controller | Signal "Global Clock FAIL" from clock controller to Board Controller and then to Backplane FPGAs. |
| Board Controller | SP1RX[0] | Backplane DFE1 RX |  |
| Board Controller | SP0RX[1] | Backplane DFE0 RX |  |
| Board Controller | SPLDR[1] | Backplane Left Driver |  |
| Board Controller | SPFE0_[2..0] | IN0 | Signal "FE_SRST_DECODE" from Board Controller to Front-End FPGAs. |
| IN0 | FECOM[3..1] | IN1..3 |  |
| IN0 | FECOM[8..6] | IN4..6 |  |
| IN0 | FECOM[13..11] | IN7..9 |  |
| IN0 | FECOM[18..16] | IN10..12 |  |
| IN0 | FECOM[23..21] | IN13..15 |  |
| Board Controller | SP0GO[1..0] | DFE0 Green-Orange | Enable output links test pattern transmission. SP0GO[0]: DFE0 Green (2 links) SP0GO[1]: DFE0 Orange |
| Board Controller | SP0PY[1..0] | DFE0 Purple-Yellow | SP0PY[0]: DFE0 Purple SP0PY[1]: DFE0 Yellow |
| Board Controller | SP0BR[1..0] | DFE0 Blue-Red | SP0BR[0]: DFE0 Blue SP0BR[1]: DFE0 Red (2 links) |
| Board Controller | SP1GO[1..0] | DFE1 Green-Orange | SP1GO[0]: DFE1 Green (2 links) SP1GO[1]: DFE1 Orange |
| Board Controller | SP1PY[1..0] | DFE1 Purple-Yellow | SP1PY[0]: DFE1 Purple SP1PY[1]: DFE1 Yellow |
| Board Controller | SP1BR[1..0] | DFE1 Blue-Red | SP1BR[0]: DFE1 Blue SP1BR[1]: DFE1 Red (2 links) |
| DFE0 Green-Orange | INTERBUS[4] | BE Spartan FPGAs | Signal TPG_RESET (Test Pattern Generators synchronous reset) generated on the DFE0 Green-Orange FPGA and sent to the other BE Spartan FPGAs in order to have the test pattern generators be synchronized on all the output links of a Mixer Board. |
| Board Controller | SPLDR[0] | Backplane Left Driver | Signal used to shutdown the CY2308 clock buffer feeding the clock to the LVDS TXs. |
| Board Controller | SPFE13_[3] | IN1..3 | Signal "LED LATCH ENABLE" used to improve diagnostic. |
| IN1..3 | FECOM[4] | IN0 |  |
| IN0 | FECOM[9] | IN4..6 |  |
| IN0 | FECOM[14] | IN7..9 |  |
| IN0 | FECOM[19] | IN10..12 |  |
| IN0 | FECOM[24] | IN13..15 |  |
| Backplane Right Driver | SPRDR[0] | Board Controller | Global Clock/SYNC error signal. |
| IN1315 | SPFE1315[2] | Board Controller | Used to propagate the GSYNC signal to the Board Controller. The signal is needed to correctly time the trigger for the Output Links FIFOs. |
| Board Controller | SP0RX[0] | DFE0 RX | Used to transmit the FIFO trigger signal generated by the board controller to the Output Links FIFOs (back-end devices). |
| DFE0 RX | INTERBUS[3] | Back-End FPGAs | Used to transmit the FIFO trigger signal generated by the board controller to the Output Links FIFOs (back-end devices). |

Table 8.1, Spare connections usage.

# Appendix C - Mixer Board Printed Circuit Board Interconnection Matrix

The interconnection matrix consists of all the printed circuit board traces used to carry data between the front-end, back-end and backplane FPGAs. The following tables show the data interconnections for each of the mixer input links and for the two backplane receivers FPGAs.

The mixer board design is required to fit four different versions of firmware, one four each of the four boards handling the data of a supersector. Because of this requirement there are some connections that are not used in each of the four firmware versions. A table cell has a grey background when the corresponding data bit has a connection to a Back-End or Backplane FPGA. A"greyed" table cell will also contain at least one of four possible numbered icons ((((() which are used to indicate the firmware version using the connection.

| Link#0 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | (((( |  |  |  |  |  |  |  |
| 2 | (((( |  |  |  |  |  |  |  |
| 3 |  | (((( |  |  |  |  |  |  |
| 4 |  | (((( |  |  |  |  |  |  |
| 5 |  | (((( |  |  |  |  |  |  |
| 6 |  |  | (((( |  |  |  |  |  |
| 7 |  |  | (((( |  |  |  |  |  |
| 8 |  |  |  | (((( |  |  |  |  |
| 9 |  |  |  | (((( |  |  |  |  |
| 10 |  |  |  |  | (((( |  |  |  |
| 11 |  |  |  |  | (((( |  |  |  |
| 12 |  |  |  |  | (((( |  |  |  |
| 13 |  |  |  |  |  | (((( |  |  |
| 14 |  |  |  |  |  | (((( |  |  |
| 15 | (((( |  |  |  |  |  |  |  |
| 16 | (((( |  |  |  |  |  |  |  |
| 17 |  | (((( |  |  |  |  |  |  |
| 18 |  | (((( |  |  |  |  |  |  |
| 19 |  | (((( |  |  |  |  |  |  |
| 20 |  |  | (((( |  |  |  |  |  |
| 21 |  |  | (((( |  |  |  |  |  |
| 22 |  |  |  | (((( |  |  |  |  |
| 23 |  |  |  | (((( |  |  |  |  |
| 24 |  |  |  |  | (((( |  |  |  |
| 25 |  |  |  |  | (((( |  |  |  |
| 26 |  |  |  |  | (((( | (((( |  |  |
| 27 |  |  |  |  |  | (((( |  |  |

Figure 9.1, Link #0 (CPS) Interconnection Matrix.

| Link#1 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | (((( |  |  |  |  |  |  |  |
| 2 | (((( |  |  |  |  |  |  |  |
| 3 | (((( |  |  |  |  |  |  |  |
| 4 | (((( |  |  |  |  |  |  |  |
| 5 | (((( |  |  |  |  |  |  |  |
| 6 | (((( |  |  |  |  |  |  |  |
| 7 | ( | ( (( |  |  |  |  |  |  |
| 8 | ( | ( (( |  |  |  |  |  |  |
| 9 |  | (((( |  |  |  |  |  |  |
| 10 |  | (((( |  |  |  |  |  |  |
| 11 |  |  | (((( |  |  |  |  |  |
| 12 |  |  | (((( |  |  |  |  |  |
| 13 |  |  | (((( |  | ( ( |  |  |  |
| 14 |  |  | ( | ( | ( ( |  |  |  |
| 15 |  |  | ( | ( (( |  |  |  |  |
| 16 |  |  |  | (((( |  |  |  |  |
| 17 |  |  |  | (((( |  |  |  |  |
| 18 |  |  |  | (((( |  |  |  |  |
| 19 |  |  |  | (((( |  |  |  |  |
| 20 |  |  |  | (((( |  |  |  |  |

Figure 9.2, Link #1 Interconnection Matrix

| Link#2 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | (((( |  |  |  |  |  |  |  |
| 2 | (((( |  |  |  |  |  |  |  |
| 3 | (((( |  |  |  |  |  |  |  |
| 4 | (((( |  |  |  |  |  |  |  |
| 5 |  | (((( |  |  |  |  |  |  |
| 6 |  | (((( |  |  |  |  |  |  |
| 7 |  | (((( |  |  |  |  |  |  |
| 8 |  | (((( |  |  |  |  |  |  |
| 9 |  | (((( |  |  |  |  |  |  |
| 10 |  | (((( |  |  |  |  |  |  |
| 11 |  |  |  | (((( |  |  |  |  |
| 12 |  |  |  | (((( |  |  |  |  |
| 13 |  |  |  | (((( |  |  |  |  |
| 14 |  |  |  | (((( |  |  |  |  |
| 15 |  |  |  |  | (((( |  |  |  |
| 16 |  |  |  |  | (((( |  |  |  |
| 17 |  |  |  |  | (((( |  |  |  |
| 18 |  |  |  |  | (((( |  |  |  |
| 19 |  |  |  |  | (((( |  |  |  |
| 20 |  |  |  |  | (((( |  |  |  |

Figure 9.3, Link #2 Interconnection Matrix

| Link#3 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 |  | (((( |  |  |  |  |  |  |
| 2 |  | (((( |  |  |  |  |  |  |
| 3 |  | (((( |  |  |  |  |  |  |
| 4 |  | (((( |  |  |  |  |  |  |
| 5 |  | (((( |  |  |  |  |  |  |
| 6 |  | (((( |  |  |  |  |  |  |
| 7 |  |  | (((( |  |  |  |  |  |
| 8 |  |  | (((( |  |  |  |  |  |
| 9 |  |  | (((( |  |  |  |  |  |
| 10 |  |  | (((( |  |  |  |  |  |
| 11 |  |  |  |  | (((( |  |  |  |
| 12 |  |  |  |  | (((( |  |  |  |
| 13 |  |  |  |  | (((( |  |  |  |
| 14 |  |  |  |  | (((( |  |  |  |
| 15 |  |  |  |  | (((( |  |  |  |
| 16 |  |  |  |  | (((( |  |  |  |
| 17 |  |  |  |  |  | (((( |  |  |
| 18 |  |  |  |  |  | (((( |  |  |
| 19 |  |  |  |  |  | (((( |  |  |
| 20 |  |  |  |  |  | (((( |  |  |

Figure 9.4, Link #3 Interconnection Matrix

| Link#4 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | (( ( | ( |  |  |  |  |  |  |
| 2 | ( ( | (((( |  |  |  |  |  |  |
| 3 |  | (((( |  |  |  |  |  |  |
| 4 |  | (((( |  |  |  |  |  |  |
| 5 |  | (((( |  |  |  |  |  |  |
| 6 |  | (((( |  |  |  |  |  |  |
| 7 |  | ( ( | ( (( |  |  |  |  |  |
| 8 |  | ( | ( (( |  |  |  |  |  |
| 9 |  | ( | ( (( |  |  |  |  |  |
| 10 |  | ( | ( (( |  |  |  |  |  |
| 11 |  |  |  | (((( |  |  |  |  |
| 12 |  |  |  | (((( |  |  |  |  |
| 13 |  |  |  | (((( |  |  |  |  |
| 14 |  |  |  | ((( | ( ( |  |  |  |
| 15 |  |  |  | ( ( | ( ( |  |  |  |
| 16 |  |  |  | ( ( | ( ( |  |  |  |
| 17 |  |  |  | ( ( | ( ( |  |  |  |
| 18 |  |  |  | ( ( | ( ( |  |  |  |
| 19 |  |  |  |  | (((( |  |  |  |
| 20 |  |  |  |  | (((( |  |  |  |

Figure 9.5, Link #4 Interconnection Matrix

| Link#5 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | ( | (( | ( |  |  |  |  |  |
| 2 | ( | (( | ( |  |  |  |  |  |
| 3 | ( | (( | ( |  |  |  |  |  |
| 4 | ( | (( | ( |  |  |  |  |  |
| 5 | ( | (( | ( |  |  |  |  |  |
| 6 |  | (( ( | ( |  |  |  |  |  |
| 7 |  | ( ( | ( ( |  |  |  |  |  |
| 8 |  | ( ( | ( | ( |  |  |  |  |
| 9 |  | ( | (( | ( |  |  |  |  |
| 10 |  | ( | (( | ( |  |  |  |  |
| 11 |  |  |  |  | (((( |  |  |  |
| 12 |  |  |  |  | (((( |  |  |  |
| 13 |  |  |  |  | (((( |  |  |  |
| 14 |  |  |  |  | (((( |  |  |  |
| 15 |  |  |  |  | (( ( | ( |  |  |
| 16 |  |  |  |  | ( | ((( |  |  |
| 17 |  |  |  |  | ( | ((( |  |  |
| 18 |  |  |  |  | ( | ((( |  |  |
| 19 |  |  |  |  | ( | ((( |  |  |
| 20 |  |  |  |  |  | ((( |  |  |

Figure 9.6, Link #5 Interconnection Matrix

| Link#6 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 |  | ( | ((( |  |  |  |  |  |
| 2 |  | ( | ((( |  |  |  |  |  |
| 3 |  | ( | ((( |  |  |  |  |  |
| 4 |  | ( | (( | ( |  |  |  |  |
| 5 |  | ( | (( | ( |  |  |  |  |
| 6 |  | ( |  | ((( |  |  |  |  |
| 7 |  | ( |  | ((( |  |  |  |  |
| 8 |  |  | ( | ((( |  |  |  |  |
| 9 |  |  | ( | ((( |  |  |  |  |
| 10 |  |  | ( | ((( |  |  |  |  |
| 11 |  |  |  | ( | (( | ( |  |  |
| 12 |  |  |  | ( | (( | ( |  |  |
| 13 |  |  |  | ( |  | ((( |  |  |
| 14 |  |  |  |  | ( | ((( |  |  |
| 15 |  |  |  |  | ( | ((( |  |  |
| 16 |  |  |  |  | ( | ((( |  |  |
| 17 |  |  |  |  | ( | ((( |  |  |
| 18 |  |  |  |  | ( | ((( |  |  |
| 19 |  |  |  |  | ( | ((( |  |  |
| 20 |  |  |  |  | ( | ((( |  |  |

Figure 9.7, Link #6 Interconnection Matrix

| Link#7 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | ( ( |  |  |  |  | ( ( |  |  |
| 2 | ( ( |  |  |  |  | ( ( |  |  |
| 3 | ( ( |  |  |  |  | ( ( |  |  |
| 4 | ( ( |  |  |  |  | ( ( |  |  |
| 5 | ( ( |  |  |  |  | ( ( |  |  |
| 6 |  |  |  |  |  |  | ( ( | ( ( |
| 7 |  |  |  |  |  |  | ( ( | ( ( |
| 8 |  |  |  |  |  |  | ( ( | ( ( |
| 9 |  |  |  |  |  |  | ( ( | ( ( |
| 10 |  |  |  |  |  |  | ( ( | ( ( |
| 11 | ( ( | ( ( |  |  |  |  |  |  |
| 12 | ( ( | ( ( |  |  |  |  |  |  |
| 13 | ( ( |  | ( ( |  |  |  |  |  |
| 14 | ( ( |  | ( ( |  |  |  |  |  |
| 15 | ( ( | ( ( | ( ( |  |  |  |  |  |
| 16 |  | ( ( | ( ( |  |  |  |  |  |
| 17 |  | ( ( | ( ( |  |  |  |  |  |
| 18 |  |  | (((( |  |  |  |  |  |
| 19 |  |  | (((( |  |  |  |  |  |
| 20 |  |  | (((( |  |  |  |  |  |

Figure 9.8, Link #7 Interconnection Matrix

| Link#8 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | ( ( |  |  |  | ( ( | ( ( |  |  |
| 2 | ( ( |  |  |  |  | ( ( |  |  |
| 3 | ( ( |  |  |  |  | ( ( |  |  |
| 4 | ( ( |  |  |  |  | ( ( |  |  |
| 5 | ( ( |  |  |  |  | ( ( |  |  |
| 6 |  |  |  |  |  |  | ( ( | ( ( |
| 7 |  |  |  |  |  |  | ( ( | ( ( |
| 8 |  |  |  |  |  |  | ( ( | ( ( |
| 9 |  |  |  |  |  |  | ( ( | ( ( |
| 10 |  |  |  |  |  |  | ( ( | ( ( |
| 11 |  | (((( |  |  |  |  |  |  |
| 12 |  | (((( | ( ( |  |  |  |  |  |
| 13 |  | ( ( | (((( |  |  |  |  |  |
| 14 |  |  | (((( |  |  |  |  |  |
| 15 |  |  | (((( |  |  |  |  |  |
| 16 |  |  | (((( |  |  |  |  |  |
| 17 |  |  | (((( |  |  |  |  |  |
| 18 |  |  |  | (((( |  |  |  |  |
| 19 |  |  |  | (((( |  |  |  |  |
| 20 |  |  |  | (((( |  |  |  |  |

Figure 9.9, Link #8 Interconnection Matrix

| Link#9 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 |  |  | ( | ( |  |  | (( |  |
| 2 |  |  | ( | ( |  |  | (( |  |
| 3 |  |  | ( | ( |  |  | (( |  |
| 4 |  |  | ( | ( | ( |  | (( |  |
| 5 |  |  | ( |  | ( |  | (( |  |
| 6 |  |  | ( |  | ( |  | (( |  |
| 7 |  |  | ( |  | ( |  | (( |  |
| 8 |  |  |  | ( | ( |  | (( |  |
| 9 |  |  |  | ( |  | ( | (( |  |
| 10 |  |  |  | ( |  | ( | (( |  |
| 11 | ( | ((( |  |  |  |  |  |  |
| 12 | ( | ((( |  |  |  |  |  |  |
| 13 | ( | ((( | ( |  |  |  |  |  |
| 14 | ( | (( | ( |  |  |  |  |  |
| 15 | ( | (( | ( |  |  |  |  |  |
| 16 | ( | (( | ( |  |  |  |  |  |
| 17 | ( | ( | (( |  |  |  |  |  |
| 18 | ( |  | (( | ( |  |  |  |  |
| 19 | ( |  | (( | ( |  |  |  |  |
| 20 | ( |  | (( | ( |  |  |  |  |

Figure 9.10, Link #9 Interconnection Matrix

| Link#10 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | ( |  |  |  | ( |  |  | (( |
| 2 | ( |  |  |  | ( |  |  | (( |
| 3 | ( |  |  |  | ( |  |  | (( |
| 4 | ( |  |  |  | ( |  |  | (( |
| 5 | ( |  |  |  |  | ( |  | (( |
| 6 |  | ( |  |  |  | ( |  | (( |
| 7 |  | ( |  |  |  | ( |  | (( |
| 8 |  | ( |  |  |  | ( |  | (( |
| 9 |  | ( |  |  |  | ( |  | (( |
| 10 |  | ( |  |  |  | ( |  | (( |
| 11 |  |  |  | ((( | ( |  |  |  |
| 12 |  |  |  | ((( | ( |  |  |  |
| 13 |  |  |  | (( | ( ( |  |  |  |
| 14 |  |  |  |  | (((( |  |  |  |
| 15 |  |  |  |  | (((( |  |  |  |
| 16 |  |  |  |  | ((( | ( |  |  |
| 17 |  |  |  |  | ((( | ( |  |  |
| 18 |  |  |  |  | ((( | ( |  |  |
| 19 |  |  |  |  | ((( | ( |  |  |
| 20 |  |  |  |  | ((( | ( |  |  |

Figure 9.11, Link #10 Interconnection Matrix

| Link#11 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | ( |  |  | ( |  |  |  | (( |
| 2 | ( |  |  | ( |  |  |  | (( |
| 3 | ( |  |  | ( | ( |  |  | (( |
| 4 | ( |  |  |  | ( |  |  | (( |
| 5 | ( |  |  |  | ( |  |  | (( |
| 6 |  | ( |  |  |  | ( |  | (( |
| 7 |  | ( |  |  |  | ( |  | (( |
| 8 |  | ( |  |  |  | ( |  | (( |
| 9 |  | ( |  |  |  | ( |  | (( |
| 10 |  | ( |  |  |  | ( |  | (( |
| 11 |  |  |  | ( | (( | ( |  |  |
| 12 |  |  |  | ( | (( | ( |  |  |
| 13 |  |  |  |  | ( ( | ( ( |  |  |
| 14 |  |  |  |  | ( ( | ( ( |  |  |
| 15 |  |  |  |  | ( ( | ( ( |  |  |
| 16 |  |  |  |  | ( | (( ( |  |  |
| 17 |  |  |  |  | ( | (( ( |  |  |
| 18 |  |  |  |  | ( | (( ( |  |  |
| 19 |  |  |  |  | ( | (( ( |  |  |
| 20 |  |  |  |  | ( | (( ( |  |  |

Figure 9.12, Link #11 Interconnection Matrix

| Link#12 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 | ( |  |  | ( |  |  | ( | ( |
| 2 | ( |  |  | ( |  |  | ( | ( |
| 3 | ( |  |  | ( |  |  | ( | ( |
| 4 | ( |  |  | ( |  |  | ( | ( |
| 5 | ( |  |  |  | ( |  | ( | ( |
| 6 | ( |  |  |  | ( |  | ( | ( |
| 7 | ( |  |  |  | ( |  | ( | ( |
| 8 | ( |  |  |  | ( |  | ( | ( |
| 9 |  | ( |  |  | ( |  | ( | ( |
| 10 |  | ( |  |  | ( |  | ( | ( |
| 11 |  |  | (((( |  |  |  |  |  |
| 12 |  |  | (((( |  |  |  |  |  |
| 13 |  |  | (((( |  |  |  |  |  |
| 14 |  |  | ( | ((( |  |  |  |  |
| 15 |  |  | ( | ((( |  |  |  |  |
| 16 |  |  |  | (((( |  |  |  |  |
| 17 |  |  |  | (((( |  |  |  |  |
| 18 |  |  |  | (((( | ((( |  |  |  |
| 19 |  |  |  | ( | ((( |  |  |  |
| 20 |  |  |  | ( | ((( |  |  |  |

Figure 9.13, Link #12 Interconnection Matrix

| Link#13 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 |  |  |  |  |  |  | ( | ((( |
| 2 |  |  |  |  |  |  | ( | ((( |
| 3 |  |  |  |  |  |  | ( | ((( |
| 4 |  |  |  |  |  |  | ( | ((( |
| 5 |  |  |  |  |  |  | ( | ((( |
| 6 |  |  |  |  |  |  | ( | ((( |
| 7 |  |  |  |  |  |  | ( | ((( |
| 8 |  |  |  |  |  |  | ( | ((( |
| 9 |  |  |  |  |  |  | ( | ((( |
| 10 |  |  |  |  |  |  | ( | ((( |
| 11 |  |  |  | (( ( | ( |  |  |  |
| 12 |  |  |  | (( ( | ( |  |  |  |
| 13 |  |  |  | (( ( | ( |  |  |  |
| 14 |  |  |  | (( ( | (( |  |  |  |
| 15 |  |  |  |  | (((( |  |  |  |
| 16 |  |  |  |  | (((( |  |  |  |
| 17 |  |  |  |  | (( | ( ( |  |  |
| 18 |  |  |  |  | (( | ( ( |  |  |
| 19 |  |  |  |  | ( | (( ( |  |  |
| 20 |  |  |  |  |  | (((( |  |  |

Figure 9.14, Link #13 Interconnection Matrix

| Link#14 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 |  |  |  |  |  |  | ((( | ( |
| 2 |  |  |  |  |  |  | ((( | ( |
| 3 |  |  |  |  |  |  | ((( | ( |
| 4 |  |  |  |  |  |  | ((( | ( |
| 5 |  |  |  |  |  |  | ((( | ( |
| 6 |  |  |  |  |  |  | ((( | ( |
| 7 |  |  |  |  |  |  | ((( | ( |
| 8 |  |  |  |  |  |  | ((( | ( |
| 9 |  |  |  |  |  |  | ((( | ( |
| 10 |  |  |  |  |  |  | ((( | ( |
| 11 |  |  | (((( |  |  |  |  |  |
| 12 |  |  | (((( |  |  |  |  |  |
| 13 |  |  | (((( |  |  |  |  |  |
| 14 |  |  | (((( |  |  |  |  |  |
| 15 |  |  | (((( |  |  |  |  |  |
| 16 |  | ( |  | ( (( |  |  |  |  |
| 17 |  | ( |  | ( (( |  |  |  |  |
| 18 |  | ( |  | (((( |  |  |  |  |
| 19 |  |  |  | (((( |  |  |  |  |
| 20 |  |  |  | (((( |  |  |  |  |

Figure 9.15, Link #14 Interconnection Matrix

| Link#15 |  | DFE0 |  |  | DFE1 |  | Backplane driver |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Yellow Purple | Red Blue | Green Orange | Yellow Purple | Red Blue | Left | Right |
| 1 |  |  |  |  |  |  | ((( | ( |
| 2 |  |  |  |  |  |  | ((( | ( |
| 3 |  |  |  |  |  |  | ((( | ( |
| 4 |  |  |  |  |  |  | ((( | ( |
| 5 |  |  |  |  |  |  | ((( | ( |
| 6 |  |  |  |  |  |  | ((( | ( |
| 7 |  |  |  |  |  |  | ((( | ( |
| 8 |  |  |  |  |  |  | ((( | ( |
| 9 |  |  |  |  |  |  | ((( | ( |
| 10 |  |  |  |  |  |  | ((( | ( |
| 11 | (((( |  |  |  |  |  |  |  |
| 12 | (((( |  |  |  |  |  |  |  |
| 13 | (((( |  |  |  |  |  |  |  |
| 14 | (((( |  |  |  |  |  |  |  |
| 15 | (( | ( ( |  |  |  |  |  |  |
| 16 | ( | ( (( |  |  |  |  |  |  |
| 17 |  | (( | ( ( |  |  |  |  |  |
| 18 |  | (( | ( ( |  |  |  |  |  |
| 19 |  | (( | ( ( |  |  |  |  |  |
| 20 |  | (( | ( ( |  |  |  |  |  |

Figure 9.16, Link #15 Interconnection Matrix

| 0GRN_ORG | DFE0 | 0YEL_PUR | DFE0 | 0RED_BLU | DFE0 |
| --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Bit# | Yellow Purple | Bit# | Red Blue |
| 1 | ((( | 1 | ((( | 1 | (((( |
| 2 | ((( | 2 | ((( | 2 | (((( |
| 3 | ((( | 3 | ((( | 3 | (((( |
| 4 | ((( | 4 | ((( | 4 | (( |
| 5 | ((( | 5 | ((( | 5 | (( |
| 6 | ((( | 6 | ((( | 6 | (( |
| 7 | ((( | 7 | ((( | 7 | (( |
| 8 | ((( | 8 | (( | 8 | (( |
| 9 | ((( | 9 | (( | 9 | (( |
| 10 | ((( | 10 | (( | 10 | ( |
| 11 | ((( | 11 | (( |  |  |
| 12 | ((( | 12 | (( |  |  |
| 13 | ((( | 13 | (( |  |  |
| 14 | ((( | 14 | (( |  |  |
| 15 | ((( | 15 | (( |  |  |
| 16 | ((( | 16 | (( |  |  |
| 17 | ((( | 17 | (( |  |  |
| 18 | ((( | 18 | ( |  |  |
| 19 | ((( | 19 | ( |  |  |
| 20 | ( | 20 |  |  |  |
| 21 | ( | 21 |  |  |  |
| 22 | ( | 22 |  |  |  |
| 23 | ( |  |  |  |  |
| 24 | ( |  |  |  |  |
| 25 | ( |  |  |  |  |
| 26 | ( |  |  |  |  |

Figure 9.17, Backplane DFE0 Receiver Interconnection Matrix.

| 1GRN_ORG | DFE1 | 1YEL_PUR | DFE1 | 1RED_BLU | DFE1 |
| --- | --- | --- | --- | --- | --- |
| Bit# | Green Orange | Bit# | Yellow Purple | Bit# | Red Blue |
| 1 | ((( | 1 | ((( | 1 | ((( |
| 2 | ((( | 2 | ((( | 2 | ((( |
| 3 | ((( | 3 | ((( | 3 | ((( |
| 4 | ((( | 4 | ((( | 4 | ((( |
| 5 | (( | 5 | ((( | 5 | ((( |
| 6 | ( | 6 | ((( | 6 | ((( |
| 7 | ( | 7 | ((( | 7 | ((( |
| 8 | ( | 8 | (( | 8 | ((( |
| 9 | ( | 9 | ( | 9 | ((( |
| 10 | ( | 10 | ( | 10 | ((( |
| 11 | ( | 11 | ( | 11 | ((( |
| 12 | ( | 12 | ( | 12 | ((( |
|  |  | 13 | ( | 13 | ((( |
|  |  | 14 | ( | 14 | ((( |
|  |  | 15 |  | 15 | ((( |
|  |  |  |  | 16 | ((( |
|  |  |  |  | 17 | ((( |
|  |  |  |  | 18 | ((( |
|  |  |  |  | 19 | ((( |
|  |  |  |  | 20 | (( |
|  |  |  |  | 21 | (( |
|  |  |  |  | 22 | ( |
|  |  |  |  | 23 | ( |
|  |  |  |  | 24 |  |
|  |  |  |  | 25 |  |
|  |  |  |  | 26 |  |
|  |  |  |  | 27 |  |
|  |  |  |  | 28 |  |
|  |  |  |  | 29 |  |
|  |  |  |  | 30 |  |

Figure 9.18, Backplane DFE1 Receiver Interconnection Matrix.

# Appendix D - Mixer System Backplane connectors pinout

| Pin # | Row ‘z’ (bottom shield) | Row ‘a’ | Row ‘b’ | Row ‘c’ | Row ‘d’ | Row ‘e’ | Row ‘f’ (top shield) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | GND | INLFT2 | GND | INLFT1 | GND | OUTRT1 |  |
| 2 |  | GND | INLFT3 | GND | OUTRT2 | GND | GND |
| 3 | GND | INLFT4 | GND | OUTRT3 | GND | OUTRT4 |  |
| 4 |  | GND | INLFT5 | GND | OUTRT5 | GND | GND |
| 5 | GND | INLFT7 | GND | INLFT6 | GND | OUTRT6 |  |
| 6 |  | GND | INLFT8 | GND | OUTRT7 | GND | GND |
| 7 | GND | INLFT9 | GND | OUTRT8 | GND | OUTRT9 |  |
| 8 |  | GND | INLFT10 | GND | OUTRT10 | GND | GND |
| 9 | GND | INLFT12 | GND | INLFT11 | GND | OUTRT11 |  |
| 10 |  | GND | INLFT13 | GND | OUTRT12 | GND | GND |
| 11 | GND | INLFT14 | GND | OUTRT13 | GND | OUTRT14 |  |
|  | polarizing and guiding peg |
| 12 | GND | GND | INLFT15 | GND | OUTRT15 | GND |  |
| 13 |  | INLFT17 | GND | INLFT16 | GND | OUTRT16 | GND |
| 14 | GND | GND | INLFT18 | GND | OUTRT17 | GND |  |
| 15 |  | INLFT19 | GND | OUTRT18 | GND | OUTRT19 | GND |
| 16 | GND | GND | INLFT20 | GND | OUTRT20 | GND |  |
| 17 |  | INLFT22 | GND | INLFT21 | GND | OUTRT21 | GND |
| 18 | GND | GND | INLFT23 | GND | OUTRT22 | GND |  |
| 19 |  | INLFT24 | GND | OUTRT23 | GND | OUTRT24 | GND |
| 20 | GND | GND | INLFT25 | GND | OUTRT25 | GND |  |
| 21 |  | INLFT27 | GND | INLFT26 | GND | OUTRT26 | GND |
| 22 | GND | GND | INLFT28 | GND | OUTRT27 | GND |  |
| 1 |  | INLFT29 | GND | OUTRT28 | GND | OUTRT29 | GND |
| 2 | GND | GND | INLFT30 | GND | OUTRT30 | GND |  |
| 3 |  | INLFT32 | GND | INLFT31 | GND | OUTRT31 | GND |
| 4 | GND | GND | INLFT33 | GND | OUTRT32 | GND |  |
| 5 |  | INLFT34 | GND | OUTRT33 | GND | OUTRT34 | GND |
| 6 | GND | GND | INLFT35 | GND | OUTRT35 | GND |  |
| 7 |  | INLFT37 | GND | INLFT36 | GND | OUTRT36 | GND |
| 8 | GND | GND | INLFT38 | GND | OUTRT37 | GND |  |
| 9 |  | INLFT39 | GND | OUTRT38 | GND | OUTRT39 | GND |
| 10 | GND | GND | INLFT40 | GND | OUTRT40 | GND |  |
| 11 |  | GND | GND | INLFT41 | GND | OUTRT41 | GND |
| 12 | GND | MOD_ID4 | MOD_ID3 | MOD_ID2 | MOD_ID1 | MOD_ID0 |  |
| 13 |  | +IN_CLK | GND | +OUT_CLK0 | +OUT_CLK1 | +OUT_CLK2 | GND |
| 14 | GND | -IN_CLK | GND | -OUT_CLK0 | -OUT_CLK1 | -OUT_CLK2 |  |
| 15 |  | GND | GND | GND | GND | GND | GND |
| 16 | GND | STAT_CLK | GND | STAT_RST | GND | STAT |  |
| 17 |  | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | GND |
| 18 | GND | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V |  |
| 19 |  | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | GND |

Table 10.1, Pin/Signal assignments for the backplane top section connector

| Pin # | Row ‘z’ (bottom shield) | Row ‘a’ | Row ‘b’ | Row ‘c’ | Row ‘d’ | Row ‘e’ | Row ‘f’ (top shield) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | GND | VADDR7 | VWRITE | VDAT6 | VDAT5 | VDAT2 |  |
| 2 |  | VADDR15 | *SYSRST | VDAT7 | VDAT0 | VDAT3 | GND |
| 3 | GND | VADDR12 | VAS | VSYSCLK | VDAT1 | VDAT4 |  |
| 4 |  | VADDR9 | *VDTACK | *VBERR | VADDR13 | VADDR5 | GND |
| 5 | GND | VADDR11 | VADDR2 | VADDR10 | VADDR0 | VADDR3 |  |
| 6 |  | VADDR8 | VADDR6 | VADDR1 | VADDR14 | VADDR4 | GND |
| 7 | GND | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V |  |
| 8 |  | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | Power 3.3V | GND |
| 9 | GND | OUTLFT2 | GND | OUTLFT1 | GND | INRT1 |  |
| 10 |  | GND | OUTLFT3 | GND | INRT2 | GND | GND |
| 11 | GND | OUTLFT4 | GND | INRT3 | GND | INRT4 |  |
|  | polarizing and guiding peg |
| 12 | GND | GND | OUTLFT5 | GND | INRT5 | GND |  |
| 13 |  | OUTLFT7 | GND | OUTLFT6 | GND | INRT6 | GND |
| 14 | GND | GND | OUTLFT8 | GND | INRT7 | GND |  |
| 15 |  | OUTLFT9 | GND | INRT8 | GND | INRT9 | GND |
| 16 | GND | GND | OUTLFT10 | GND | INRT10 | GND |  |
| 17 |  | OUTLFT12 | GND | OUTLFT11 | GND | INRT11 | GND |
| 18 | GND | GND | OUTLFT13 | GND | INRT12 | GND |  |
| 19 |  | OUTLFT14 | GND | INRT13 | GND | INRT14 | GND |
| 20 | GND | GND | OUTLFT15 | GND | INRT15 | GND |  |
| 21 |  | OUTLFT17 | GND | OUTLFT16 | GND | INRT16 | GND |
| 22 | GND | GND | OUTLFT18 | GND | INRT17 | GND |  |
| 1 |  | OUTLFT19 | GND | INRT18 | GND | INRT19 | GND |
| 2 | GND | GND | OUTLFT20 | GND | INRT20 | GND |  |
| 3 |  | OUTLFT22 | GND | OUTLFT21 | GND | INRT21 | GND |
| 4 | GND | GND | OUTLFT23 | GND | INRT22 | GND |  |
| 5 |  | OUTLFT24 | GND | INRT23 | GND | INRT24 | GND |
| 6 | GND | GND | OUTLFT25 | GND | INRT25 | GND |  |
| 7 |  | OUTLFT27 | GND | OUTLFT26 | GND | INRT26 | GND |
| 8 | GND | GND | OUTLFT28 | GND | INRT27 | GND |  |
| 9 |  | OUTLFT29 | GND | INRT28 | GND | INRT29 | GND |
| 10 | GND | GND | OUTLFT30 | GND | INRT30 | GND |  |
| 11 |  | OUTLFT32 | GND | OUTLFT31 | GND | INRT31 | GND |
| 12 | GND | GND | OUTLFT33 | GND | INRT32 | GND |  |
| 13 |  | OUTLFT34 | GND | INRT33 | GND | INRT34 | GND |
| 14 | GND | GND | OUTLFT35 | GND | INRT35 | GND |  |
| 15 |  | OUTLFT37 | GND | OUTLFT36 | GND | INRT36 | GND |
| 16 | GND | GND | OUTLFT38 | GND | INRT37 | GND |  |
| 17 |  | OUTLFT39 | GND | INRT38 | GND | INRT39 | GND |
| 18 | GND | GND | OUTLFT40 | GND | INRT40 | GND |  |
| 19 |  | GND | GND | OUTLFT41 | GND | INRT41 | GND |

Table 10.2, Pin/Signal assignments for the backplane bottom section connector.

# Appendix E - Test Patterns specification

## Input links test patterns

The Mixer Board logic allows for recognition of two test patterns, a walking one (shown in Table 11.1) and a walking zero (the complementary pattern of the walking one with the exclusion of the SYNC bit). The pattern detection can be verified by setting the LEDs to monitoring mode #2 (walking 1) and mode #3 (walking 0). The pattern recognition feature is used to test input links integrity and to verifying the correctness of cabling.

The word at time slot #42 is used by the test pattern detection logic to synchronize itself with the test pattern received on the input link. No synchronization check is performed between the test patterns received on different links.

| Time | Bit number (Top Half Link) | Bit number (Bottom Half Link) | Sync bit |
| --- | --- | --- | --- |
| Slot | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 2 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 3 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 4 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 5 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 6 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 7 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 11 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 12 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 13 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 14 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 15 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 16 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 17 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 18 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 19 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 21 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 22 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 23 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 24 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 25 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 26 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 27 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 30 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 31 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 32 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 33 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 34 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 35 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 |
| 36 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 37 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 39 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 40 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 41 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 42 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 43 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 44 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 45 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 46 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 47 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 48 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 49 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |
| 50 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 51 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 52 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 53 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 54 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 55 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 56 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 |
| 57 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 58 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 59 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 60 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 61 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 62 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 63 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 64 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 65 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 66 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 67 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 68 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 69 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 70 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |

Table 11.1, Input Links walking 1 test pattern.

## Output links test patterns

The mixer board output links can send a test pattern instead of data. The test pattern is the same for every output link except for a link-identification word (Table 11.3), which is unique between all the links in a mixer subsystem. The DFE board logic is able to recognize the test pattern generated by the mixer. This feature allows verifying both link integrity and correctness of cabling.

The test pattern transmission can be enabled through the Output Links Test Mode registers (see Paragraph 4.5.13 page 41).

| Time | Bit number |
| --- | --- |
| Slot | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |
| 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |
| 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 |
| 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |
| 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 11 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 14 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 17 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 18 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 19 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 21 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 22 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 23 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 24 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 25 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 26 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 27 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 28 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 29 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Relative Sector | Link Color |

Table 11.2, Output Links test patterns.

| Link Color | Link color identifier |  | Relative Sector | Relative Sector # within a supersector | Mixer Board # | Mixer Board link color and link# |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | red |  | 0 | 0 | 0 | 0 | 1 | 1 | green[00, 01], orange[02], purple[03] |
| 0 | 0 | 1 | green |  | 0 | 0 | 0 | 1 | 2 | 1 | yellow[04], blue[05], red[06] |
| 0 | 1 | 0 | blue |  | 0 | 0 | 1 | 0 | 3 | 1 | green[10, 11], orange[12], purple[13] |
| 0 | 1 | 1 | yellow |  | 0 | 0 | 1 | 1 | 4 | 1 | yellow[14], blue[15], red[16] |
| 1 | 0 | 0 | purple |  | 0 | 1 | 0 | 0 | 5 | 2 | green[00, 01], orange[02], purple[03] |
| 1 | 0 | 1 | orange |  | 0 | 1 | 0 | 1 | 6 | 2 | yellow[04], blue[05], red[06] |
|  |  |  |  |  | 0 | 1 | 1 | 0 | 7 | 2 | green[10, 11], orange[12], purple[13] |
|  |  |  |  |  | 0 | 1 | 1 | 1 | 8 | 2 | yellow[14], blue[15], red[16] |
|  |  |  |  |  | 1 | 0 | 0 | 0 | 9 | 3 | green[00, 01], orange[02], purple[03] |
|  |  |  |  |  | 1 | 0 | 0 | 1 | 10 | 3 | yellow[04], blue[05], red[06] |
|  |  |  |  |  | 1 | 0 | 1 | 0 | 11 | 3 | green[10, 11], orange[12], purple[13] |
|  |  |  |  |  | 1 | 0 | 1 | 1 | 12 | 3 | yellow[14], blue[15], red[16] |
|  |  |  |  |  | 1 | 1 | 0 | 0 | 13 | 4 | green[00, 01], orange[02], purple[03] |
|  |  |  |  |  | 1 | 1 | 0 | 1 | 14 | 4 | yellow[04], blue[05], red[06] |
|  |  |  |  |  | 1 | 1 | 1 | 0 | 15 | 4 | green[10, 11], orange[12], purple[13] |
|  |  |  |  |  | 1 | 1 | 1 | 1 | 16 | 4 | yellow[14], blue[15], red[16] |

Table 11.3, Link relative sector and color encoding in the output links test pattern.

# Appendix F – Mixer Board Components and Layout

Table 12.1 list the components used on the mixer board with the exclusions of resistors, capacitors, inductors and minor stock components. A complete list of all components is available in a separate document [Ref. 8]. Figure 12.1 is a drawning of the mixer board showing components location.

| Component | Schematic and Layout identifier/s | Description |
| --- | --- | --- |
| AMP 2510-6003UB | CON1, CON3. | 10 pin JTAG header. [Ref. 13] |
| AMP 1-106014-1 | J1, J2, J4, J6. | 125 pin front panel header. [Ref. 13] |
| AMP 2-7674004-2 | J3, J5, J7. | Surface mount header for HP Logic Analyzer. [Ref. 13] |
| Brookdale Electronics B500CTE3G | X1 | Thru hole Half-DIP 53.104 MHZ oscillator. Used as board's local clock source. [Ref. 14] |
| Cypress CY7B9911V-5JC | U9. | PLCC32 3.3V RoboClock Low Voltage programmable Skew Clock Buffer. Used as clock source for the backplane clock transmitter (U15). [Ref. 18] |
| Cypress CY2308ZC-1H | U8, U13, U16. | 16 pin TSSOP 3.3V Zero Delay Buffer. Used for on-board clock distribution. [Ref. 18] |
| C&K EP11S2D1ABE | S1 | Front panel reset push-button. [Ref. 19] |
| Elmec Delay Line | U71, U72. | 3 pin delay line. Not installed. [Ref. 20] |
| Fairchild 74LCX16244MEAX | U28, U36. | 48 pin SSOP Low Voltage 16-Bit Buffer/Line Driver. [Ref. 22] |
| Fairchild 74LCX38MX | U30. | 14 pin SOIC Low Voltage Quad 2-Input NAND Gate (open drain). [Ref. 22] |
| Harting 1721-110-2102 | P1, P3. | 110 pin keyed backplane connectors. [Ref. 24] |
| Harting 1725-095-2102 | P2, P4. | 95 pin backplane connectors. [Ref. 24] |
| IDT QS3VH126S1 | U14. | 14 pin SOIC Quickswitch® 3.3V QUAD Active High Analog Switch. Is used as clock multiplexer. [Ref. 27] |
| IDT QS53805AQ | U4, U7. | 20 pin QSSOP Low Skew 3.3V CMOS Clock Driver/Buffer. Used for configuration (CCLK) and JTAG (TCK) clocks distribution. [Ref. 27] |
| Linear Technology LTC1326CS8-2.5 | U20. | 8 pin SO (S8) MicropowerPrecision Triple Supply Monitors. Used to monitor the 3.3Volt and 2.5Volt voltages. [Ref. 29] |
| Littlefuse 251004 | F1 | 4 Ampere fuse. [Ref. 30] |
| Littlefuse 241012 | F2 | 10 Ampere fuse. [Ref. 30] |
| Lumex SSL-LX3059IGW | D2, D3, D4, D5, D7, D8, D9, D10, D11, D12, D13, D14, D15, D16, D17, D18. | Front panel bi-color LEDs. [Ref. 31] |
| Lumex SSL-LX3052DI | D1, D6 | Front panel 3.3V and 2.5V LEDs. [Ref. 31] |
| Motorola MC74LCX245DT | U27, U29, U34. | 20 pin TSSOP Low Voltage Bidirectional Transceiver. [Ref. 33] |
| Micrel MIC39500-2.5BU | U21. | TO263 5A Low-Voltage Low-Dropout Regulator. Used to generate the 2.5 Volt needed by the Virtex FPGAs (core voltage). [Ref. 32] |
| National Semiconductor DS90LV047ATMTC | U15. | 16 pin TSSOP 3V LVDS Quad CMOS Differential Line Driver. Used as backplane clock transmitter on boards operation as masters. [Ref. 34] |
| National Semiconductor DS90LV018ATM | U17. | 8 pin SOP 3V LVDS Single CMOS Differential Line Receiver. Used as backplane clock receiver on boards operating as slaves. [Ref. 34] |
| Philips 1N5908 | D19. | 1500W Zener Transient Voltage Suppressor. Used for over-voltage protection on the 3.3Volt power input. [Ref. 36] |
| Texas Instruments SN65LVDS93DGG | U53, U54, U55, U56, U57, U58, U59, U60, U61, U62, U63, U64, U65, U66, U67, U68. | TSOP LVDS SERDES Transmitter. Used as LVDS transmitter for the output links [Ref. 38]. |
| Texas Instruments SN65LVDS96DGG | U23, U24, U25, U26, U37, U38, U39, U40, U41, U42, U43, U44, U49, U50, U51. | 20 pin TSOP LVDS SERDES Receiver. Used as LVDS receiver for links 1 to 15 (21 bit wide links). [Ref. 38] |
| Texas Instruments SN65LVDS94DGG | U52. | TSOP LVDS SERDES Receiver. Used as LVDS receiver for link 0 (28 bit wide link). [Ref. 38] |
| Texas Instruments 74LCX16244T | U3, U69, U70. | 48pin TSSOP Low Voltage 16-Bit Buffer/Line Driver. [Ref. 38] |
| Xilinx XCV50-6 PQ240C | U5, U6, U12, U31, U32, U33, U45, U46, U47, U48. | PQFP240 Virtex™ 2.5Volt FPGA. Used for the Front End and Backplane FPGAs. [Ref. 40] |
| Xilinx XCS40XL-5 PQ240C | U1, U2, U10, U11, U18, U19, U22. | PQFP240 Spartan FPGA. Used for the Back-End and for the Board Controller FPGAs. [Ref. 40] |
| Xilinx XC18V01SO20C | U35. | SOIC Configuration EEPROM. Is used for the configuration of the board controller FPGA (U22). [Ref.40] |

Table 12.1, Mixer Board component list.

The Mixer printed circuit board has a total of fourteen metal layers seven of which are signal layers. Table 12.2 shows the layers stacking.

| PCB Layer | Description | Impedence control |
| --- | --- | --- |
| Top | Signal layer | 50 (± 10%) Ω coated microstrip. |
| Inner 1 | Ground plane layer | n.a. |
| Inner 2 | Signal layer | 50 (± 10%) Ω symmetrical stripline. |
| Inner 3 | 2.5 Volt power plane layer | n.a. |
| Inner 4 | Signal layer | 50 (± 10%) Ω symmetrical stripline. |
| Inner 5 | Ground plane layer | n.a. |
| Inner 6 | 3.3 Volt power plane layer | n.a. |
| Inner 7 | Signal layer | 50 (± 10%) Ω symmetrical stripline. |
| Inner 8 | Ground plane layer | n.a. |
| Inner 9 | Signal layer | 50 (± 10%) Ω symmetrical stripline. |
| Inner 10 | 3.3 Volt power plane layer | n.a. |
| Inner 11 | Signal layer | 50 (± 10%) Ω symmetrical stripline. |
| Inner 12 | Ground plane layer | n.a. |
| Bottom | Signal layer | 50 (± 10%) Ω coated microstrip. |

Table 12.2, Printed Circuit Board stacking.

Figure 12.1, Mixer Board.

# Appendix G – Input and Output Links cabling

## Mixer System Input Links cabling map

Mapping information are derived from several documents Ref[20].

| Slot # 2 | MixerB # 1 | Supersector # 4 |  |  |  | Slot # 3 | MixerB # 2 | Supersector # 4 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 1 | 59 | LHB | 2 |  | 15 | 8 | 58 | LHB | 2 |
| 14 | 5 | 56 | RHB | 1 |  | 14 | 7 | 53 | RHB | 1 |
| 13 | 1 | 59 | RHB | 3 |  | 13 | 8 | 58 | RHB | 2 |
| 12 | 6 | 57 | LHB | 1 |  | 12 | 3 | 52 | RHB | 3 |
| 11 | 5 | 56 | LHB | 4 |  | 11 | 6 | 57 | RHB | 2 |
| 10 | 3 | 52 | LHB | 1 |  | 10 | 6 | 57 | LHB | 3 |
| 9 | 8 | 58 | LHB | 1 |  | 9 | 6 | 57 | LHB | 2 |
| 8 | 3 | 52 | RHB | 4 |  | 8 | 2 | 54 | LHB | 3 |
| 7 | 7 | 53 | LHB | 4 |  | 7 | 8 | 58 | RHB | 3 |
| 6 | 6 | 57 | RHB | 4 |  | 6 | 8 | 58 | LHB | 3 |
| 5 | 2 | 54 | RHB | 1 |  | 5 | 3 | 52 | LHB | 2 |
| 4 | 8 | 58 | RHB | 4 |  | 4 | 2 | 54 | RHB | 2 |
| 3 | 4 | 55 | RHB | 1 |  | 3 | 4 | 55 | RHB | 2 |
| 2 | 4 | 55 | LHB | 4 |  | 2 | 4 | 55 | LHB | 3 |
| 1 | 2 | 54 | LHB | 4 |  | 1 | 6 | 57 | RHB | 3 |
| 0 | CPS | 70 | RHB | 2 |  | 0 | CPS | 70 | LHB | 3 |

Table 13.1, Slot#2 and Slot#3 (Supersector#4).

| Slot # 4 | MixerB # 3 | Supersector # 4 |  |  |  | Slot # 5 | MixerB # 4 | Supersector # 4 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 5 | 56 | LHB | 3 |  | 15 | 1 | 59 | LHB | 1 |
| 14 | 5 | 56 | RHB | 2 |  | 14 | 5 | 56 | LHB | 2 |
| 13 | 2 | 54 | LHB | 1 |  | 13 | 1 | 59 | RHB | 4 |
| 12 | 7 | 53 | LHB | 3 |  | 12 | 3 | 52 | LHB | 4 |
| 11 | 3 | 52 | RHB | 2 |  | 11 | 7 | 53 | RHB | 3 |
| 10 | 6 | 57 | RHB | 1 |  | 10 | 3 | 52 | RHB | 1 |
| 9 | 2 | 54 | LHB | 2 |  | 9 | 7 | 53 | LHB | 2 |
| 8 | 3 | 52 | LHB | 3 |  | 8 | 2 | 54 | RHB | 4 |
| 7 | 7 | 53 | RHB | 2 |  | 7 | 7 | 53 | LHB | 1 |
| 6 | 6 | 57 | LHB | 4 |  | 6 | 5 | 56 | RHB | 4 |
| 5 | 8 | 58 | RHB | 1 |  | 5 | 5 | 56 | RHB | 3 |
| 4 | 8 | 58 | LHB | 4 |  | 4 | 5 | 56 | LHB | 1 |
| 3 | 4 | 55 | RHB | 3 |  | 3 | 4 | 55 | RHB | 4 |
| 2 | 4 | 55 | LHB | 2 |  | 2 | 4 | 55 | LHB | 1 |
| 1 | 2 | 54 | RHB | 3 |  | 1 | 7 | 53 | RHB | 4 |
| 0 | CPS | 70 | RHB | 3 |  | 0 | CPS | 70 | LHB | 2 |

Table 13.2, Slot#4 and Slot#5 (Supersector#4).

| Slot #6 | MixerB # 1 | Supersector # 5 |  |  |  | Slot # 7 | MixerB # 2 | Supersector # 5 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 1 | 51 | LHB | 2 |  | 15 | 8 | 47 | LHB | 2 |
| 14 | 5 | 45 | RHB | 1 |  | 14 | 7 | 48 | RHB | 1 |
| 13 | 1 | 51 | RHB | 3 |  | 13 | 8 | 47 | RHB | 2 |
| 12 | 6 | 44 | LHB | 1 |  | 12 | 3 | 49 | RHB | 3 |
| 11 | 5 | 45 | LHB | 4 |  | 11 | 6 | 44 | RHB | 2 |
| 10 | 3 | 49 | LHB | 1 |  | 10 | 6 | 44 | LHB | 3 |
| 9 | 8 | 47 | LHB | 1 |  | 9 | 6 | 44 | LHB | 2 |
| 8 | 3 | 49 | RHB | 4 |  | 8 | 2 | 50 | LHB | 3 |
| 7 | 7 | 48 | LHB | 4 |  | 7 | 8 | 47 | RHB | 3 |
| 6 | 6 | 44 | RHB | 4 |  | 6 | 8 | 47 | LHB | 3 |
| 5 | 2 | 50 | RHB | 1 |  | 5 | 3 | 49 | LHB | 2 |
| 4 | 8 | 47 | RHB | 4 |  | 4 | 2 | 50 | RHB | 2 |
| 3 | 4 | 46 | RHB | 1 |  | 3 | 4 | 46 | RHB | 2 |
| 2 | 4 | 46 | LHB | 4 |  | 2 | 4 | 46 | LHB | 3 |
| 1 | 2 | 50 | LHB | 4 |  | 1 | 6 | 44 | RHB | 3 |
| 0 | CPS | 72 | RHB | 2 |  | 0 | CPS | 72 | LHB | 3 |

Table 13.3, Slot#6 and Slot#7 (Supersector#5).

| Slot # 8 | MixerB # 3 | Supersector # 5 |  |  |  | Slot # 9 | MixerB # 4 | Supersector # 5 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 5 | 45 | LHB | 3 |  | 15 | 1 | 51 | LHB | 1 |
| 14 | 5 | 45 | RHB | 2 |  | 14 | 5 | 45 | LHB | 2 |
| 13 | 2 | 50 | LHB | 1 |  | 13 | 1 | 51 | RHB | 4 |
| 12 | 7 | 48 | LHB | 3 |  | 12 | 3 | 49 | LHB | 4 |
| 11 | 3 | 49 | RHB | 2 |  | 11 | 7 | 48 | RHB | 3 |
| 10 | 6 | 44 | RHB | 1 |  | 10 | 3 | 49 | RHB | 1 |
| 9 | 2 | 50 | LHB | 2 |  | 9 | 7 | 48 | LHB | 2 |
| 8 | 3 | 49 | LHB | 3 |  | 8 | 2 | 50 | RHB | 4 |
| 7 | 7 | 48 | RHB | 2 |  | 7 | 7 | 48 | LHB | 1 |
| 6 | 6 | 44 | LHB | 4 |  | 6 | 5 | 45 | RHB | 4 |
| 5 | 8 | 47 | RHB | 1 |  | 5 | 5 | 45 | RHB | 3 |
| 4 | 8 | 47 | LHB | 4 |  | 4 | 5 | 45 | LHB | 1 |
| 3 | 4 | 46 | RHB | 3 |  | 3 | 4 | 46 | RHB | 4 |
| 2 | 4 | 46 | LHB | 2 |  | 2 | 4 | 46 | LHB | 1 |
| 1 | 2 | 50 | RHB | 3 |  | 1 | 7 | 48 | RHB | 4 |
| 0 | CPS | 72 | RHB | 3 |  | 0 | CPS | 72 | LHB | 2 |

Table 13.4, Slot#8 and Slot#9 (Supersector#5).

| Slot #10 | MixerB # 1 | Supersector # 1 |  |  |  | Slot # 11 | MixerB # 2 | Supersector # 1 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 1 | 36 | LHB | 4 |  | 15 | 8 | 43 | LHB | 2 |
| 14 | 5 | 41 | RHB | 1 |  | 14 | 7 | 39 | RHB | 1 |
| 13 | 1 | 36 | RHB | 1 |  | 13 | 8 | 43 | RHB | 2 |
| 12 | 6 | 42 | LHB | 1 |  | 12 | 3 | 38 | RHB | 3 |
| 11 | 5 | 41 | LHB | 4 |  | 11 | 6 | 42 | RHB | 2 |
| 10 | 3 | 38 | LHB | 1 |  | 10 | 6 | 42 | LHB | 3 |
| 9 | 8 | 43 | LHB | 1 |  | 9 | 6 | 42 | LHB | 2 |
| 8 | 3 | 38 | RHB | 4 |  | 8 | 2 | 37 | LHB | 3 |
| 7 | 7 | 39 | LHB | 4 |  | 7 | 8 | 43 | RHB | 3 |
| 6 | 6 | 42 | RHB | 4 |  | 6 | 8 | 43 | LHB | 3 |
| 5 | 2 | 37 | RHB | 1 |  | 5 | 3 | 38 | LHB | 2 |
| 4 | 8 | 43 | RHB | 4 |  | 4 | 2 | 37 | RHB | 2 |
| 3 | 4 | 40 | RHB | 1 |  | 3 | 4 | 40 | RHB | 2 |
| 2 | 4 | 40 | LHB | 4 |  | 2 | 4 | 40 | LHB | 3 |
| 1 | 2 | 37 | LHB | 4 |  | 1 | 6 | 42 | RHB | 3 |
| 0 | CPS | 26 | RHB | 2 |  | 0 | CPS | 26 | LHB | 3 |

Table 13.5, Slot#10 and Slot#11 (Supersector#1).

| Slot # 12 | MixerB # 3 | Supersector # 1 |  |  |  | Slot # 13 | MixerB # 4 | Supersector # 1 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 5 | 41 | LHB | 3 |  | 15 | 1 | 36 | LHB | 3 |
| 14 | 5 | 41 | RHB | 2 |  | 14 | 5 | 41 | LHB | 2 |
| 13 | 2 | 37 | LHB | 1 |  | 13 | 1 | 36 | RHB | 2 |
| 12 | 7 | 39 | LHB | 3 |  | 12 | 3 | 38 | LHB | 4 |
| 11 | 3 | 38 | RHB | 2 |  | 11 | 7 | 39 | RHB | 3 |
| 10 | 6 | 42 | RHB | 1 |  | 10 | 3 | 38 | RHB | 1 |
| 9 | 2 | 37 | LHB | 2 |  | 9 | 7 | 39 | LHB | 2 |
| 8 | 3 | 38 | LHB | 3 |  | 8 | 2 | 37 | RHB | 4 |
| 7 | 7 | 39 | RHB | 2 |  | 7 | 7 | 39 | LHB | 1 |
| 6 | 6 | 42 | LHB | 4 |  | 6 | 5 | 41 | RHB | 4 |
| 5 | 8 | 43 | RHB | 1 |  | 5 | 5 | 41 | RHB | 3 |
| 4 | 8 | 43 | LHB | 4 |  | 4 | 5 | 41 | LHB | 1 |
| 3 | 4 | 40 | RHB | 3 |  | 3 | 4 | 40 | RHB | 4 |
| 2 | 4 | 40 | LHB | 2 |  | 2 | 4 | 40 | LHB | 1 |
| 1 | 2 | 37 | RHB | 3 |  | 1 | 7 | 39 | RHB | 4 |
| 0 | CPS | 26 | RHB | 3 |  | 0 | CPS | 26 | LHB | 2 |

Table 13.6, Slot#12 and Slot#13 (Supersector#1).

| Slot #14 | MixerB # 1 | Supersector # 2 |  |  |  | Slot # 15 | MixerB # 2 | Supersector # 2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 1 | 36 | LHB | 2 |  | 15 | 8 | 32 | LHB | 2 |
| 14 | 5 | 30 | RHB | 1 |  | 14 | 7 | 33 | RHB | 1 |
| 13 | 1 | 36 | RHB | 3 |  | 13 | 8 | 32 | RHB | 2 |
| 12 | 6 | 29 | LHB | 1 |  | 12 | 3 | 34 | RHB | 3 |
| 11 | 5 | 30 | LHB | 4 |  | 11 | 6 | 29 | RHB | 2 |
| 10 | 3 | 34 | LHB | 1 |  | 10 | 6 | 29 | LHB | 3 |
| 9 | 8 | 32 | LHB | 1 |  | 9 | 6 | 29 | LHB | 2 |
| 8 | 3 | 34 | RHB | 4 |  | 8 | 2 | 35 | LHB | 3 |
| 7 | 7 | 33 | LHB | 4 |  | 7 | 8 | 32 | RHB | 3 |
| 6 | 6 | 29 | RHB | 4 |  | 6 | 8 | 32 | LHB | 3 |
| 5 | 2 | 35 | RHB | 1 |  | 5 | 3 | 34 | LHB | 2 |
| 4 | 8 | 32 | RHB | 4 |  | 4 | 2 | 35 | RHB | 2 |
| 3 | 4 | 31 | RHB | 1 |  | 3 | 4 | 31 | RHB | 2 |
| 2 | 4 | 31 | LHB | 4 |  | 2 | 4 | 31 | LHB | 3 |
| 1 | 2 | 35 | LHB | 4 |  | 1 | 6 | 29 | RHB | 3 |
| 0 | CPS | 28 | RHB | 2 |  | 0 | CPS | 28 | LHB | 3 |

Table 13.7, Slot#14 and Slot#15 (Supersector#2).

| Slot # 16 | MixerB # 3 | Supersector # 2 |  |  |  | Slot # 17 | MixerB # 4 | Supersector # 2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 5 | 30 | LHB | 3 |  | 15 | 1 | 36 | LHB | 1 |
| 14 | 5 | 30 | RHB | 2 |  | 14 | 5 | 30 | LHB | 2 |
| 13 | 2 | 35 | LHB | 1 |  | 13 | 1 | 36 | RHB | 4 |
| 12 | 7 | 33 | LHB | 3 |  | 12 | 3 | 34 | LHB | 4 |
| 11 | 3 | 34 | RHB | 2 |  | 11 | 7 | 33 | RHB | 3 |
| 10 | 6 | 29 | RHB | 1 |  | 10 | 3 | 34 | RHB | 1 |
| 9 | 2 | 35 | LHB | 2 |  | 9 | 7 | 33 | LHB | 2 |
| 8 | 3 | 34 | LHB | 3 |  | 8 | 2 | 35 | RHB | 4 |
| 7 | 7 | 33 | RHB | 2 |  | 7 | 7 | 33 | LHB | 1 |
| 6 | 6 | 29 | LHB | 4 |  | 6 | 5 | 30 | RHB | 4 |
| 5 | 8 | 32 | RHB | 1 |  | 5 | 5 | 30 | RHB | 3 |
| 4 | 8 | 32 | LHB | 4 |  | 4 | 5 | 30 | LHB | 1 |
| 3 | 4 | 31 | RHB | 3 |  | 3 | 4 | 31 | RHB | 4 |
| 2 | 4 | 31 | LHB | 2 |  | 2 | 4 | 31 | LHB | 1 |
| 1 | 2 | 35 | RHB | 3 |  | 1 | 7 | 33 | RHB | 4 |
| 0 | CPS | 28 | RHB | 3 |  | 0 | CPS | 28 | LHB | 2 |

Table 13.8, Slot#16 and Slot#17 (Supersector#2).

| Slot #18 | MixerB # 1 | Supersector # 3 |  |  |  | Slot # 19 | MixerB # 2 | Supersector # 3 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 1 | 59 | LHB | 4 |  | 15 | 8 | 66 | LHB | 2 |
| 14 | 5 | 63 | RHB | 1 |  | 14 | 7 | 65 | RHB | 1 |
| 13 | 1 | 59 | RHB | 1 |  | 13 | 8 | 66 | RHB | 2 |
| 12 | 6 | 64 | LHB | 1 |  | 12 | 3 | 61 | RHB | 3 |
| 11 | 5 | 63 | LHB | 4 |  | 11 | 6 | 64 | RHB | 2 |
| 10 | 3 | 61 | LHB | 1 |  | 10 | 6 | 64 | LHB | 3 |
| 9 | 8 | 66 | LHB | 1 |  | 9 | 6 | 64 | LHB | 2 |
| 8 | 3 | 61 | RHB | 4 |  | 8 | 2 | 60 | LHB | 3 |
| 7 | 7 | 65 | LHB | 4 |  | 7 | 8 | 66 | RHB | 3 |
| 6 | 6 | 64 | RHB | 4 |  | 6 | 8 | 66 | LHB | 3 |
| 5 | 2 | 60 | RHB | 1 |  | 5 | 3 | 61 | LHB | 2 |
| 4 | 8 | 66 | RHB | 4 |  | 4 | 2 | 60 | RHB | 2 |
| 3 | 4 | 62 | RHB | 1 |  | 3 | 4 | 62 | RHB | 2 |
| 2 | 4 | 62 | LHB | 4 |  | 2 | 4 | 62 | LHB | 3 |
| 1 | 2 | 60 | LHB | 4 |  | 1 | 6 | 64 | RHB | 3 |
| 0 | CPS | 68 | RHB | 2 |  | 0 | CPS | 68 | LHB | 3 |

Table 13.9, Slot#18 and Slot#19 (Supersector#3).

| Slot # 20 | MixerB # 3 | Supersector # 3 |  |  |  | Slot # 21 | MixerB # 4 | Supersector # 3 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | AFE relative Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |  | Mixer Link# | AFE Cassette | AFE absolute Cassette | AFE LHB/RHB | AFE Link# |
| 15 | 5 | 63 | LHB | 3 |  | 15 | 1 | 59 | LHB | 3 |
| 14 | 5 | 63 | RHB | 2 |  | 14 | 5 | 63 | LHB | 2 |
| 13 | 2 | 60 | LHB | 1 |  | 13 | 1 | 59 | RHB | 2 |
| 12 | 7 | 65 | LHB | 3 |  | 12 | 3 | 61 | LHB | 4 |
| 11 | 3 | 61 | RHB | 2 |  | 11 | 7 | 65 | RHB | 3 |
| 10 | 6 | 64 | RHB | 1 |  | 10 | 3 | 61 | RHB | 1 |
| 9 | 2 | 60 | LHB | 2 |  | 9 | 7 | 65 | LHB | 2 |
| 8 | 3 | 61 | LHB | 3 |  | 8 | 2 | 60 | RHB | 4 |
| 7 | 7 | 65 | RHB | 2 |  | 7 | 7 | 65 | LHB | 1 |
| 6 | 6 | 64 | LHB | 4 |  | 6 | 5 | 63 | RHB | 4 |
| 5 | 8 | 66 | RHB | 1 |  | 5 | 5 | 63 | RHB | 3 |
| 4 | 8 | 66 | LHB | 4 |  | 4 | 5 | 63 | LHB | 1 |
| 3 | 4 | 62 | RHB | 3 |  | 3 | 4 | 62 | RHB | 4 |
| 2 | 4 | 62 | LHB | 2 |  | 2 | 4 | 62 | LHB | 1 |
| 1 | 2 | 60 | RHB | 3 |  | 1 | 7 | 65 | RHB | 4 |
| 0 | CPS | 68 | RHB | 3 |  | 0 | CPS | 68 | LHB | 2 |

Table 13.10, Slot#20 and Slot#21 (Supersector#3).

## Mixer System Input Links cabling map organized by cassette

| Absolute Cassette# 26 | Relative Cassette# CPS |  |  |  | Absolute Cassette# 28 | Relative Cassette# CPS |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 |  |  |  |  | L | 1 |  |  |  |
| L | 2 | 13 [4] | 0 | 1 |  | L | 2 | 17 [4] | 0 | 2 |
| L | 3 | 11 [2] | 0 | 1 |  | L | 3 | 15 [2] | 0 | 2 |
| L | 4 |  |  |  |  | L | 4 |  |  |  |
| R | 1 |  |  |  |  | R | 1 |  |  |  |
| R | 2 | 10 [1] | 0 | 1 |  | R | 2 | 14 [1] | 0 | 2 |
| R | 3 | 12 [3] | 0 | 1 |  | R | 3 | 16 [3] | 0 | 2 |
| R | 4 |  |  |  |  | R | 4 |  |  |  |

Table 13.11, AFE Cassettes 26 (CPS) and 28 (CPS).

| Absolute Cassette# 29 | Relative Cassette# 6 |  |  |  | Absolute Cassette# 30 | Relative Cassette# 5 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 14 [1] | 12 | 2 |  | L | 1 | 17 [4] | 4 | 2 |
| L | 2 | 15 [2] | 9 | 2 |  | L | 2 | 17 [4] | 14 | 2 |
| L | 3 | 15 [2] | 10 | 2 |  | L | 3 | 16 [3] | 15 | 2 |
| L | 4 | 16 [3] | 6 | 2 |  | L | 4 | 14 [1] | 11 | 2 |
| R | 1 | 16 [3] | 10 | 2 |  | R | 1 | 14 [1] | 14 | 2 |
| R | 2 | 15 [2] | 11 | 2 |  | R | 2 | 16 [3] | 14 | 2 |
| R | 3 | 15 [2] | 1 | 2 |  | R | 3 | 17 [4] | 5 | 2 |
| R | 4 | 14 [1] | 6 | 2 |  | R | 4 | 17 [4] | 6 | 2 |

Table 13.12, AFE Cassettes 29 and 30.

| Absolute Cassette# 31 | Relative Cassette# 4 |  |  |  | Absolute Cassette# 32 | Relative Cassette# 8 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 17 [4] | 2 | 2 |  | L | 1 | 14 [1] | 9 | 2 |
| L | 2 | 16 [3] | 2 | 2 |  | L | 2 | 15 [2] | 15 | 2 |
| L | 3 | 15 [2] | 2 | 2 |  | L | 3 | 15 [2] | 6 | 2 |
| L | 4 | 14 [1] | 2 | 2 |  | L | 4 | 16 [3] | 4 | 2 |
| R | 1 | 14 [1] | 3 | 2 |  | R | 1 | 16 [3] | 5 | 2 |
| R | 2 | 15 [2] | 3 | 2 |  | R | 2 | 15 [2] | 13 | 2 |
| R | 3 | 16 [3] | 3 | 2 |  | R | 3 | 15 [2] | 7 | 2 |
| R | 4 | 17 [4] | 3 | 2 |  | R | 4 | 14 [1] | 4 | 2 |

Table 13.13, AFE Cassettes 31 and 32

| Absolute Cassette# 33 | Relative Cassette# 7 |  |  |  | Absolute Cassette# 34 | Relative Cassette# 3 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 17 [4] | 7 | 2 |  | L | 1 | 14 [1] | 10 | 2 |
| L | 2 | 17 [4] | 9 | 2 |  | L | 2 | 15 [2] | 5 | 2 |
| L | 3 | 16 [3] | 12 | 2 |  | L | 3 | 16 [3] | 8 | 2 |
| L | 4 | 14 [1] | 7 | 2 |  | L | 4 | 17 [4] | 12 | 2 |
| R | 1 | 15 [2] | 14 | 2 |  | R | 1 | 17 [4] | 10 | 2 |
| R | 2 | 16 [3] | 7 | 2 |  | R | 2 | 16 [3] | 11 | 2 |
| R | 3 | 17 [4] | 11 | 2 |  | R | 3 | 15 [2] | 12 | 2 |
| R | 4 | 17 [4] | 1 | 2 |  | R | 4 | 14 [1] | 8 | 2 |

Table 13.14, AFE Cassettes 33 and 34

| Absolute Cassette# 35 | Relative Cassette# 2 |  |  |  | Absolute Cassette# 36 | Relative Cassette# 1 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 16 [3] | 13 | 2 |  | L | 1 | 17 [4] | 15 | 2 |
| L | 2 | 16 [3] | 9 | 2 |  | L | 2 | 14 [1] | 15 | 2 |
| L | 3 | 15 [2] | 8 | 2 |  | L | 3 | 13 [4] | 15 | 1 |
| L | 4 | 14 [1] | 1 | 2 |  | L | 4 | 10 [1] | 15 | 1 |
| R | 1 | 14 [1] | 5 | 2 |  | R | 1 | 10 [1] | 13 | 1 |
| R | 2 | 15 [2] | 4 | 2 |  | R | 2 | 13 [4] | 13 | 1 |
| R | 3 | 16 [3] | 1 | 2 |  | R | 3 | 14 [1] | 13 | 2 |
| R | 4 | 17 [4] | 8 | 2 |  | R | 4 | 17 [4] | 13 | 2 |

Table 13.15, AFE Cassettes 35 and 36

| Absolute Cassette# 37 | Relative Cassette# 2 |  |  |  | Absolute Cassette# 38 | Relative Cassette# 3 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 12 [3] | 13 | 1 |  | L | 1 | 10 [1] | 10 | 1 |
| L | 2 | 12 [3] | 9 | 1 |  | L | 2 | 11 [2] | 5 | 1 |
| L | 3 | 11 [2] | 8 | 1 |  | L | 3 | 12 [3] | 8 | 1 |
| L | 4 | 10 [1] | 1 | 1 |  | L | 4 | 13 [4] | 12 | 1 |
| R | 1 | 10 [1] | 5 | 1 |  | R | 1 | 13 [4] | 10 | 1 |
| R | 2 | 11 [2] | 4 | 1 |  | R | 2 | 12 [3] | 11 | 1 |
| R | 3 | 12 [3] | 1 | 1 |  | R | 3 | 11 [2] | 12 | 1 |
| R | 4 | 13 [4] | 8 | 1 |  | R | 4 | 10 [1] | 8 | 1 |

Table 13.16, AFE Cassettes 37 and 38

| Absolute Cassette# 39 | Relative Cassette# 7 |  |  |  | Absolute Cassette# 40 | Relative Cassette#4 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 13 [4] | 7 | 1 |  | L | 1 | 13 [4] | 2 | 1 |
| L | 2 | 13 [4] | 9 | 1 |  | L | 2 | 12 [3] | 2 | 1 |
| L | 3 | 12 [3] | 12 | 1 |  | L | 3 | 11 [2] | 2 | 1 |
| L | 4 | 10 [1] | 7 | 1 |  | L | 4 | 10 [1] | 2 | 1 |
| R | 1 | 11 [2] | 14 | 1 |  | R | 1 | 10 [1] | 3 | 1 |
| R | 2 | 12 [3] | 7 | 1 |  | R | 2 | 11 [2] | 3 | 1 |
| R | 3 | 13 [4] | 11 | 1 |  | R | 3 | 12 [3] | 3 | 1 |
| R | 4 | 13 [4] | 1 | 1 |  | R | 4 | 13 [4] | 3 | 1 |

Table 13.17, AFE Cassettes 39 and 40

| Absolute Cassette#41 | Relative Cassette#5 |  |  |  | Absolute Cassette#42 | Relative Cassette#6 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 13 [4] | 4 | 1 |  | L | 1 | 10 [1] | 12 | 1 |
| L | 2 | 13 [4] | 14 | 1 |  | L | 2 | 11 [2] | 9 | 1 |
| L | 3 | 12 [3] | 15 | 1 |  | L | 3 | 11 [2] | 10 | 1 |
| L | 4 | 10 [1] | 11 | 1 |  | L | 4 | 12 [3] | 6 | 1 |
| R | 1 | 10 [1] | 14 | 1 |  | R | 1 | 12 [3] | 10 | 1 |
| R | 2 | 12 [3] | 14 | 1 |  | R | 2 | 11 [2] | 11 | 1 |
| R | 3 | 13 [4] | 5 | 1 |  | R | 3 | 11 [2] | 1 | 1 |
| R | 4 | 13 [4] | 6 | 1 |  | R | 4 | 10 [1] | 6 | 1 |

Table 13.18, AFE Cassettes 41 and 42

| Absolute Cassette#43 | Relative Cassette#8 |  |  |  | Absolute Cassette#44 | Relative Cassette#6 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 10 [1] | 9 | 1 |  | L | 1 | 6 [1] | 12 | 5 |
| L | 2 | 11 [2] | 15 | 1 |  | L | 2 | 7 [2] | 9 | 5 |
| L | 3 | 11 [2] | 6 | 1 |  | L | 3 | 7 [2] | 10 | 5 |
| L | 4 | 12 [3] | 4 | 1 |  | L | 4 | 8 [3] | 6 | 5 |
| R | 1 | 12 [3] | 5 | 1 |  | R | 1 | 8 [3] | 10 | 5 |
| R | 2 | 11 [2] | 13 | 1 |  | R | 2 | 7 [2] | 11 | 5 |
| R | 3 | 11 [2] | 7 | 1 |  | R | 3 | 7 [2] | 1 | 5 |
| R | 4 | 10 [1] | 4 | 1 |  | R | 4 | 6 [1] | 6 | 5 |

Table 13.19, AFE Cassettes 43 and 44

| Absolute Cassette#45 | Relative Cassette#5 |  |  |  | Absolute Cassette#46 | Relative Cassette#4 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 9 [4] | 4 | 5 |  | L | 1 | 9 [4] | 2 | 5 |
| L | 2 | 9 [4] | 14 | 5 |  | L | 2 | 8 [3] | 2 | 5 |
| L | 3 | 8 [3] | 15 | 5 |  | L | 3 | 7 [2] | 2 | 5 |
| L | 4 | 6 [1] | 11 | 5 |  | L | 4 | 6 [1] | 2 | 5 |
| R | 1 | 6 [1] | 14 | 5 |  | R | 1 | 6 [1] | 3 | 5 |
| R | 2 | 8 [3] | 14 | 5 |  | R | 2 | 7 [2] | 3 | 5 |
| R | 3 | 9 [4] | 5 | 5 |  | R | 3 | 8 [3] | 3 | 5 |
| R | 4 | 9 [4] | 6 | 5 |  | R | 4 | 9 [4] | 3 | 5 |

Table 13.20, AFE Cassettes 45 and 46

| Absolute Cassette#47 | Relative Cassette#8 |  |  |  | Absolute Cassette#48 | Relative Cassette#7 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 6 [1] | 9 | 5 |  | L | 1 | 9 [4] | 7 | 5 |
| L | 2 | 7 [2] | 15 | 5 |  | L | 2 | 9 [4] | 9 | 5 |
| L | 3 | 7 [2] | 6 | 5 |  | L | 3 | 8 [3] | 12 | 5 |
| L | 4 | 8 [3] | 4 | 5 |  | L | 4 | 6 [1] | 7 | 5 |
| R | 1 | 8 [3] | 5 | 5 |  | R | 1 | 7 [2] | 14 | 5 |
| R | 2 | 7 [2] | 13 | 5 |  | R | 2 | 8 [3] | 7 | 5 |
| R | 3 | 7 [2] | 7 | 5 |  | R | 3 | 9 [4] | 11 | 5 |
| R | 4 | 6 [1] | 4 | 5 |  | R | 4 | 9 [4] | 1 | 5 |

Table 13.21, AFE Cassettes 47 and 48

| Absolute Cassette#49 | Relative Cassette#3 |  |  |  | Absolute Cassette#50 | Relative Cassette#2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 6 [1] | 10 | 5 |  | L | 1 | 8 [3] | 13 | 5 |
| L | 2 | 7 [2] | 5 | 5 |  | L | 2 | 8 [3] | 9 | 5 |
| L | 3 | 8 [3] | 8 | 5 |  | L | 3 | 7 [2] | 8 | 5 |
| L | 4 | 9 [4] | 12 | 5 |  | L | 4 | 6 [1] | 1 | 5 |
| R | 1 | 9 [4] | 10 | 5 |  | R | 1 | 6 [1] | 5 | 5 |
| R | 2 | 8 [3] | 11 | 5 |  | R | 2 | 7 [2] | 4 | 5 |
| R | 3 | 7 [2] | 12 | 5 |  | R | 3 | 8 [3] | 1 | 5 |
| R | 4 | 6 [1] | 8 | 5 |  | R | 4 | 9 [4] | 8 | 5 |

Table 13.22, AFE Cassettes 49 and 50

| Absolute Cassette#51 | Relative Cassette#1 |  |  |  | Absolute Cassette#52 | Relative Cassette#3 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 9 [4] | 15 | 5 |  | L | 1 | 2 [1] | 10 | 4 |
| L | 2 | 6 [1] | 15 | 5 |  | L | 2 | 3 [2] | 5 | 4 |
| L | 3 |  |  |  |  | L | 3 | 4 [3] | 8 | 4 |
| L | 4 |  |  |  |  | L | 4 | 5 [4] | 12 | 4 |
| R | 1 |  |  |  |  | R | 1 | 5 [4] | 10 | 4 |
| R | 2 |  |  |  |  | R | 2 | 4 [3] | 11 | 4 |
| R | 3 | 6 [1] | 13 | 5 |  | R | 3 | 3 [2] | 12 | 4 |
| R | 4 | 9 [4] | 13 | 5 |  | R | 4 | 2 [1] | 8 | 4 |

Table 13.23, AFE Cassettes 51 and 52

| Absolute Cassette#53 | Relative Cassette#7 |  |  |  | Absolute Cassette#54 | Relative Cassette#2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 5 [4] | 7 | 4 |  | L | 1 | 4 [3] | 13 | 4 |
| L | 2 | 5 [4] | 9 | 4 |  | L | 2 | 4 [3] | 9 | 4 |
| L | 3 | 4 [3] | 12 | 4 |  | L | 3 | 3 [2] | 8 | 4 |
| L | 4 | 2 [1] | 7 | 4 |  | L | 4 | 2 [1] | 1 | 4 |
| R | 1 | 3 [2] | 14 | 4 |  | R | 1 | 2 [1] | 5 | 4 |
| R | 2 | 4 [3] | 7 | 4 |  | R | 2 | 3 [2] | 4 | 4 |
| R | 3 | 5 [4] | 11 | 4 |  | R | 3 | 4 [3] | 1 | 4 |
| R | 4 | 5 [4] | 1 | 4 |  | R | 4 | 5 [4] | 8 | 4 |

Table 13.24, AFE Cassettes 53 and 54

| Absolute Cassette#55 | Relative Cassette#4 |  |  |  | Absolute Cassette#56 | Relative Cassette#5 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 5 [4] | 2 | 4 |  | L | 1 | 5 [4] | 4 | 4 |
| L | 2 | 4 [3] | 2 | 4 |  | L | 2 | 5 [4] | 14 | 4 |
| L | 3 | 3 [2] | 2 | 4 |  | L | 3 | 4 [3] | 15 | 4 |
| L | 4 | 2 [1] | 2 | 4 |  | L | 4 | 2 [1] | 11 | 4 |
| R | 1 | 2 [1] | 3 | 4 |  | R | 1 | 2 [1] | 14 | 4 |
| R | 2 | 3 [2] | 3 | 4 |  | R | 2 | 4 [3] | 14 | 4 |
| R | 3 | 4 [3] | 3 | 4 |  | R | 3 | 5 [4] | 5 | 4 |
| R | 4 | 5 [4] | 3 | 4 |  | R | 4 | 5 [4] | 6 | 4 |

Table 13.25, AFE Cassettes 55 and 56

| Absolute Cassette#57 | Relative Cassette#6 |  |  |  | Absolute Cassette#58 | Relative Cassette#8 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 2 [1] | 12 | 4 |  | L | 1 | 2 [1] | 9 | 4 |
| L | 2 | 3 [2] | 9 | 4 |  | L | 2 | 3 [2] | 15 | 4 |
| L | 3 | 3 [2] | 10 | 4 |  | L | 3 | 3 [2] | 6 | 4 |
| L | 4 | 4 [3] | 6 | 4 |  | L | 4 | 4 [3] | 4 | 4 |
| R | 1 | 4 [3] | 10 | 4 |  | R | 1 | 4 [3] | 5 | 4 |
| R | 2 | 3 [2] | 11 | 4 |  | R | 2 | 3 [2] | 13 | 4 |
| R | 3 | 3 [2] | 1 | 4 |  | R | 3 | 3 [2] | 7 | 4 |
| R | 4 | 2 [1] | 6 | 4 |  | R | 4 | 2 [1] | 4 | 4 |

Table 13.26, AFE Cassettes 57 and 58

| Absolute Cassette#59 | Relative Cassette#1 |  |  |  | Absolute Cassette#60 | Relative Cassette#2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 5 [4] | 15 | 4 |  | L | 1 | 20 [3] | 13 | 3 |
| L | 2 | 2 [1] | 15 | 4 |  | L | 2 | 20 [3] | 9 | 3 |
| L | 3 | 21 [4] | 15 | 3 |  | L | 3 | 19 [2] | 8 | 3 |
| L | 4 | 18 [1] | 15 | 3 |  | L | 4 | 18 [1] | 1 | 3 |
| R | 1 | 18 [1] | 13 | 3 |  | R | 1 | 18 [1] | 5 | 3 |
| R | 2 | 21 [4] | 13 | 3 |  | R | 2 | 19 [2] | 4 | 3 |
| R | 3 | 2 [1] | 13 | 4 |  | R | 3 | 20 [3] | 1 | 3 |
| R | 4 | 5 [4] | 13 | 4 |  | R | 4 | 21 [4] | 8 | 3 |

Table 13.27, AFE Cassettes 59 and 60

| Absolute Cassette#61 | Relative Cassette#3 |  |  |  | Absolute Cassette#62 | Relative Cassette#4 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 18 [1] | 10 | 3 |  | L | 1 | 21 [4] | 2 | 3 |
| L | 2 | 19 [2] | 5 | 3 |  | L | 2 | 20 [3] | 2 | 3 |
| L | 3 | 20 [3] | 8 | 3 |  | L | 3 | 19 [2] | 2 | 3 |
| L | 4 | 21 [4] | 12 | 3 |  | L | 4 | 18 [1] | 2 | 3 |
| R | 1 | 21 [4] | 10 | 3 |  | R | 1 | 18 [1] | 3 | 3 |
| R | 2 | 20 [3] | 11 | 3 |  | R | 2 | 19 [2] | 3 | 3 |
| R | 3 | 19 [2] | 12 | 3 |  | R | 3 | 20 [3] | 3 | 3 |
| R | 4 | 18 [1] | 8 | 3 |  | R | 4 | 21 [4] | 3 | 3 |

Table 13.28, AFE Cassettes 61 and 62

| Absolute Cassette#63 | Relative Cassette#5 |  |  |  | Absolute Cassette#64 | Relative Cassette#6 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 21 [4] | 4 | 3 |  | L | 1 | 18 [1] | 12 | 3 |
| L | 2 | 21 [4] | 14 | 3 |  | L | 2 | 19 [2] | 9 | 3 |
| L | 3 | 20 [3] | 15 | 3 |  | L | 3 | 19 [2] | 10 | 3 |
| L | 4 | 18 [1] | 11 | 3 |  | L | 4 | 20 [3] | 6 | 3 |
| R | 1 | 18 [1] | 14 | 3 |  | R | 1 | 20 [3] | 10 | 3 |
| R | 2 | 20 [3] | 14 | 3 |  | R | 2 | 19 [2] | 11 | 3 |
| R | 3 | 21 [4] | 5 | 3 |  | R | 3 | 19 [2] | 1 | 3 |
| R | 4 | 21 [4] | 6 | 3 |  | R | 4 | 18 [1] | 6 | 3 |

Table 13.29, AFE Cassettes 63 and 64

| Absolute Cassette#65 | Relative Cassette#7 |  |  |  | Absolute Cassette#66 | Relative Cassette#8 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 | 21 [4] | 7 | 3 |  | L | 1 | 18 [1] | 9 | 3 |
| L | 2 | 21 [4] | 9 | 3 |  | L | 2 | 19 [2] | 15 | 3 |
| L | 3 | 20 [3] | 12 | 3 |  | L | 3 | 19 [2] | 6 | 3 |
| L | 4 | 18 [1] | 7 | 3 |  | L | 4 | 20 [3] | 4 | 3 |
| R | 1 | 19 [2] | 14 | 3 |  | R | 1 | 20 [3] | 5 | 3 |
| R | 2 | 20 [3] | 7 | 3 |  | R | 2 | 19 [2] | 13 | 3 |
| R | 3 | 21 [4] | 11 | 3 |  | R | 3 | 19 [2] | 7 | 3 |
| R | 4 | 21 [4] | 1 | 3 |  | R | 4 | 18 [1] | 4 | 3 |

Table 13.30, AFE Cassettes 65 and 66

| Absolute Cassette# 68 | Relative Cassette# CPS |  |  |  | Absolute Cassette# 70 | Relative Cassette# CPS |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  | L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |
| L | 1 |  |  |  |  | L | 1 |  |  |  |
| L | 2 | 21 [4] | 0 | 3 |  | L | 2 | 5 [4] | 0 | 4 |
| L | 3 | 19 [2] | 0 | 3 |  | L | 3 | 3 [2] | 0 | 4 |
| L | 4 |  |  |  |  | L | 4 |  |  |  |
| R | 1 |  |  |  |  | R | 1 |  |  |  |
| R | 2 | 18 [1] | 0 | 3 |  | R | 2 | 2 [1] | 0 | 4 |
| R | 3 | 20 [3] | 0 | 3 |  | R | 3 | 4 [3] | 0 | 4 |
| R | 4 |  |  |  |  | R | 4 |  |  |  |

Table 13.31, AFE Cassettes 68 (CPS) and 70 (CPS).

| Absolute Cassette# 72 | Relative Cassette# CPS |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L/R | AFE Link# | Mixer Slot # [MB#] | Mixer Link# | Super Sector # |  |  |  |  |  |  |
| L | 1 |  |  |  |  |  |  |  |  |  |
| L | 2 | 9 [4] | 0 | 5 |  |  |  |  |  |  |
| L | 3 | 7 [2] | 0 | 5 |  |  |  |  |  |  |
| L | 4 |  |  |  |  |  |  |  |  |  |
| R | 1 |  |  |  |  |  |  |  |  |  |
| R | 2 | 6 [1] | 0 | 5 |  |  |  |  |  |  |
| R | 3 | 8 [3] | 0 | 5 |  |  |  |  |  |  |
| R | 4 |  |  |  |  |  |  |  |  |  |

Table 13.32, AFE Cassette 72 (CPS).

| Relative | Absolute Cassette Number |
| --- | --- |
| Cassette# | Super sector 1 | Super sector 2 | Super sector 3 | Super sector 4 | Super sector 5 |
| 1 | 36(Module 1-4) | 36(Module 5-8) | 59(Module 1-4) | 59(Module 5-8) | 51(Module 5-8) |
| 2 | 37 | 35 | 60 | 54 | 50 |
| 3 | 38 | 34 | 61 | 52 | 49 |
| 4 | 40 | 31 | 62 | 55 | 46 |
| 5 | 41 | 30 | 63 | 56 | 45 |
| 6 | 42 | 29 | 64 | 57 | 44 |
| 7 | 39 | 33 | 65 | 53 | 48 |
| 8 | 43 | 32 | 66 | 58 | 47 |
| CPS | 26 | 28 | 68 | 70 | 72 |

Table 13.33, Relative and Absolute Cassette numbers.

## Mixer System Output Links cabling map

| Mixer board output links arrangement on the front panel |  | DFE board input links arrangement on the front panel |  |
| --- | --- | --- | --- |
| Mixer Link# | Link Color [DFE Link#] | Mixer Link PORT# (for cabling) |  | DFE Link# | Link Color | DFE Link PORT# (for cabling) |
| Row of pins used for JTAG |  | 1 unused row of pins |
| 17 | Red [0] | 1 |  | 0 | Red (copy) | 1 |
| 16 | Red [5] | 2 |  | 2 unused row of pins |
| 15 | Blue [7] | 3 |  | 1 | not used. | 2 |
| 14 | Yellow [6] | 4 |  | 2 unused row of pins |
| 13 | Purple [3] | 5 |  | 2 | Orange | 3 |
| 12 | Orange [2] | 6 |  | 2 unused row of pins |
| 11 | Green [4] | 7 |  | 4 | Green | 4 |
| 10 | Green [9] | 8 |  | 2 unused row of pins |
| Unused row of pins |  | 3 | Purple | 5 |
| 07 | Red [0] | 9 |  | 2 unused row of pins |
| 06 | Red [5] | 10 |  | 5 | Red | 6 |
| 05 | Blue [7] | 11 |  | 2 unused row of pins |
| 04 | Yellow [6] | 12 |  | 7 | Blue | 7 |
| 03 | Purple [3] | 13 |  | 2 unused row of pins |
| 02 | Orange [2] | 14 |  | 6 | Yellow | 8 |
| 01 | Green [4] | 15 |  | 2 unused row of pins |
| 00 | Green [9] | 16 |  | 8 | not used | 9 |
|  |  |  |  | 2 unused row of pins |
|  |  |  |  | 9 | Green (copy) | 10 |
|  |  |  |  | 1 unused row of pins |

Table 13.34, Mixer Board output links and DFE input links arrangements on the front panels.

| Slot# 2 | MB# 1 | Supersector# 4 |  |  | Slot# 3 | MB# 2 | Supersector# 4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-3 | 4 |  | 17 | Red [L0-P1] | PC03-3 | 6 |
| 16 | Red [L5-P6] | PC03-3 | 3 |  | 16 | Red [L5-P6] | PC03-3 | 5 |
| 15 | Blue [L7-P7] | PC03-3 | 3 |  | 15 | Blue [L7-P7] | PC03-3 | 5 |
| 14 | Yellow [L6-P8] | PC03-3 | 3 |  | 14 | Yellow [L6-P8] | PC03-3 | 5 |
| 13 | Purple [L3-P5] | PC03-3 | 3 |  | 13 | Purple [L3-P5] | PC03-3 | 5 |
| 12 | Orange [L2-P3] | PC03-3 | 3 |  | 12 | Orange [L2-P3] | PC03-3 | 5 |
| 11 | Green [L4-P4] | PC03-3 | 3 |  | 11 | Green [L4-P4] | PC03-3 | 5 |
| 10 | Green [L9-P10] | PC03-3 | 2 |  | 10 | Green [L9-P10] | PC03-3 | 4 |
| 07 | Red [L0-P1] | PC03-3 | 3 |  | 07 | Red [L0-P1] | PC03-3 | 5 |
| 06 | Red [L5-P6] | PC03-3 | 2 |  | 06 | Red [L5-P6] | PC03-3 | 4 |
| 05 | Blue [L7-P7] | PC03-3 | 2 |  | 05 | Blue [L7-P7] | PC03-3 | 4 |
| 04 | Yellow [L6-P8] | PC03-3 | 2 |  | 04 | Yellow [L6-P8] | PC03-3 | 4 |
| 03 | Purple [L3-P5] | PC03-3 | 2 |  | 03 | Purple [L3-P5] | PC03-3 | 4 |
| 02 | Orange [L2-P3] | PC03-3 | 2 |  | 02 | Orange [L2-P3] | PC03-3 | 4 |
| 01 | Green [L4-P4] | PC03-3 | 2 |  | 01 | Green [L4-P4] | PC03-3 | 4 |
| 00 | Green [L9-P10] | PC03-2 | 21 |  | 00 | Green [L9-P10] | PC03-3 | 3 |

Table 13.35, Slot#2 and Slot#3 (Supersector#4).

| Slot# 4 | MB# 3 | Supersector# 4 |  |  | Slot# 5 | MB# 4 | Supersector# 4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-3 | 8 |  | 17 | Red [L0-P1] | PC03-3 | 10 |
| 16 | Red [L5-P6] | PC03-3 | 7 |  | 16 | Red [L5-P6] | PC03-3 | 9 |
| 15 | Blue [L7-P7] | PC03-3 | 7 |  | 15 | Blue [L7-P7] | PC03-3 | 9 |
| 14 | Yellow [L6-P8] | PC03-3 | 7 |  | 14 | Yellow [L6-P8] | PC03-3 | 9 |
| 13 | Purple [L3-P5] | PC03-3 | 7 |  | 13 | Purple [L3-P5] | PC03-3 | 9 |
| 12 | Orange [L2-P3] | PC03-3 | 7 |  | 12 | Orange [L2-P3] | PC03-3 | 9 |
| 11 | Green [L4-P4] | PC03-3 | 7 |  | 11 | Green [L4-P4] | PC03-3 | 9 |
| 10 | Green [L9-P10] | PC03-3 | 6 |  | 10 | Green [L9-P10] | PC03-3 | 8 |
| 07 | Red [L0-P1] | PC03-3 | 7 |  | 07 | Red [L0-P1] | PC03-3 | 9 |
| 06 | Red [L5-P6] | PC03-3 | 6 |  | 06 | Red [L5-P6] | PC03-3 | 8 |
| 05 | Blue [L7-P7] | PC03-3 | 6 |  | 05 | Blue [L7-P7] | PC03-3 | 8 |
| 04 | Yellow [L6-P8] | PC03-3 | 6 |  | 04 | Yellow [L6-P8] | PC03-3 | 8 |
| 03 | Purple [L3-P5] | PC03-3 | 6 |  | 03 | Purple [L3-P5] | PC03-3 | 8 |
| 02 | Orange [L2-P3] | PC03-3 | 6 |  | 02 | Orange [L2-P3] | PC03-3 | 8 |
| 01 | Green [L4-P4] | PC03-3 | 6 |  | 01 | Green [L4-P4] | PC03-3 | 8 |
| 00 | Green [L9-P10] | PC03-3 | 5 |  | 00 | Green [L9-P10] | PC03-3 | 7 |

Table 13.36, Slot#4 and Slot#5 (Supersector#4).

| Slot# 6 | MB# 1 | Supersector# 5 |  |  | Slot# 7 | MB# 2 | Supersector# 5 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-3 | 12 |  | 17 | Red [L0-P1] | PC03-3 | 14 |
| 16 | Red [L5-P6] | PC03-3 | 11 |  | 16 | Red [L5-P6] | PC03-3 | 13 |
| 15 | Blue [L7-P7] | PC03-3 | 11 |  | 15 | Blue [L7-P7] | PC03-3 | 13 |
| 14 | Yellow [L6-P8] | PC03-3 | 11 |  | 14 | Yellow [L6-P8] | PC03-3 | 13 |
| 13 | Purple [L3-P5] | PC03-3 | 11 |  | 13 | Purple [L3-P5] | PC03-3 | 13 |
| 12 | Orange [L2-P3] | PC03-3 | 11 |  | 12 | Orange [L2-P3] | PC03-3 | 13 |
| 11 | Green [L4-P4] | PC03-3 | 11 |  | 11 | Green [L4-P4] | PC03-3 | 13 |
| 10 | Green [L9-P10] | PC03-3 | 10 |  | 10 | Green [L9-P10] | PC03-3 | 12 |
| 07 | Red [L0-P1] | PC03-3 | 11 |  | 07 | Red [L0-P1] | PC03-3 | 13 |
| 06 | Red [L5-P6] | PC03-3 | 10 |  | 06 | Red [L5-P6] | PC03-3 | 12 |
| 05 | Blue [L7-P7] | PC03-3 | 10 |  | 05 | Blue [L7-P7] | PC03-3 | 12 |
| 04 | Yellow [L6-P8] | PC03-3 | 10 |  | 04 | Yellow [L6-P8] | PC03-3 | 12 |
| 03 | Purple [L3-P5] | PC03-3 | 10 |  | 03 | Purple [L3-P5] | PC03-3 | 12 |
| 02 | Orange [L2-P3] | PC03-3 | 10 |  | 02 | Orange [L2-P3] | PC03-3 | 12 |
| 01 | Green [L4-P4] | PC03-3 | 10 |  | 01 | Green [L4-P4] | PC03-3 | 12 |
| 00 | Green [L9-P10] | PC03-3 | 9 |  | 00 | Green [L9-P10] | PC03-3 | 11 |

Table 13.37, Slot#6 and Slot#7 (Supersector#5).

| Slot# 8 | MB# 3 | Supersector# 5 |  |  | Slot# 9 | MB# 4 | Supersector# 5 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-3 | 16 |  | 17 | Red [L0-P1] | PC03-3 | 18 |
| 16 | Red [L5-P6] | PC03-3 | 15 |  | 16 | Red [L5-P6] | PC03-3 | 17 |
| 15 | Blue [L7-P7] | PC03-3 | 15 |  | 15 | Blue [L7-P7] | PC03-3 | 17 |
| 14 | Yellow [L6-P8] | PC03-3 | 15 |  | 14 | Yellow [L6-P8] | PC03-3 | 17 |
| 13 | Purple [L3-P5] | PC03-3 | 15 |  | 13 | Purple [L3-P5] | PC03-3 | 17 |
| 12 | Orange [L2-P3] | PC03-3 | 15 |  | 12 | Orange [L2-P3] | PC03-3 | 17 |
| 11 | Green [L4-P4] | PC03-3 | 15 |  | 11 | Green [L4-P4] | PC03-3 | 17 |
| 10 | Green [L9-P10] | PC03-3 | 14 |  | 10 | Green [L9-P10] | PC03-3 | 16 |
| 07 | Red [L0-P1] | PC03-3 | 15 |  | 07 | Red [L0-P1] | PC03-3 | 17 |
| 06 | Red [L5-P6] | PC03-3 | 14 |  | 06 | Red [L5-P6] | PC03-3 | 16 |
| 05 | Blue [L7-P7] | PC03-3 | 14 |  | 05 | Blue [L7-P7] | PC03-3 | 16 |
| 04 | Yellow [L6-P8] | PC03-3 | 14 |  | 04 | Yellow [L6-P8] | PC03-3 | 16 |
| 03 | Purple [L3-P5] | PC03-3 | 14 |  | 03 | Purple [L3-P5] | PC03-3 | 16 |
| 02 | Orange [L2-P3] | PC03-3 | 14 |  | 02 | Orange [L2-P3] | PC03-3 | 16 |
| 01 | Green [L4-P4] | PC03-3 | 14 |  | 01 | Green [L4-P4] | PC03-3 | 16 |
| 00 | Green [L9-P10] | PC03-3 | 13 |  | 00 | Green [L9-P10] | PC03-3 | 15 |

Table 13.38, Slot#8 and Slot#9 (Supersector#5).

| Slot# 10 | MB# 1 | Supersector# 1 |  |  | Slot# 11 | MB# 2 | Supersector# 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-3 | 20 |  | 17 | Red [L0-P1] | PC03-2 | 2 |
| 16 | Red [L5-P6] | PC03-3 | 19 |  | 16 | Red [L5-P6] | PC03-3 | 21 |
| 15 | Blue [L7-P7] | PC03-3 | 19 |  | 15 | Blue [L7-P7] | PC03-3 | 21 |
| 14 | Yellow [L6-P8] | PC03-3 | 19 |  | 14 | Yellow [L6-P8] | PC03-3 | 21 |
| 13 | Purple [L3-P5] | PC03-3 | 19 |  | 13 | Purple [L3-P5] | PC03-3 | 21 |
| 12 | Orange [L2-P3] | PC03-3 | 19 |  | 12 | Orange [L2-P3] | PC03-3 | 21 |
| 11 | Green [L4-P4] | PC03-3 | 19 |  | 11 | Green [L4-P4] | PC03-3 | 21 |
| 10 | Green [L9-P10] | PC03-3 | 18 |  | 10 | Green [L9-P10] | PC03-3 | 20 |
| 07 | Red [L0-P1] | PC03-3 | 19 |  | 07 | Red [L0-P1] | PC03-3 | 21 |
| 06 | Red [L5-P6] | PC03-3 | 18 |  | 06 | Red [L5-P6] | PC03-3 | 20 |
| 05 | Blue [L7-P7] | PC03-3 | 18 |  | 05 | Blue [L7-P7] | PC03-3 | 20 |
| 04 | Yellow [L6-P8] | PC03-3 | 18 |  | 04 | Yellow [L6-P8] | PC03-3 | 20 |
| 03 | Purple [L3-P5] | PC03-3 | 18 |  | 03 | Purple [L3-P5] | PC03-3 | 20 |
| 02 | Orange [L2-P3] | PC03-3 | 18 |  | 02 | Orange [L2-P3] | PC03-3 | 20 |
| 01 | Green [L4-P4] | PC03-3 | 18 |  | 01 | Green [L4-P4] | PC03-3 | 20 |
| 00 | Green [L9-P10] | PC03-3 | 17 |  | 00 | Green [L9-P10] | PC03-3 | 19 |

Table 13.39, Slot#10 and Slot#11 (Supersector#1).

| Slot# 12 | MB# 3 | Supersector# 1 |  |  | Slot# 13 | MB# 4 | Supersector# 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-2 | 4 |  | 17 | Red [L0-P1] | PC03-2 | 6 |
| 16 | Red [L5-P6] | PC03-2 | 3 |  | 16 | Red [L5-P6] | PC03-2 | 5 |
| 15 | Blue [L7-P7] | PC03-2 | 3 |  | 15 | Blue [L7-P7] | PC03-2 | 5 |
| 14 | Yellow [L6-P8] | PC03-2 | 3 |  | 14 | Yellow [L6-P8] | PC03-2 | 5 |
| 13 | Purple [L3-P5] | PC03-2 | 3 |  | 13 | Purple [L3-P5] | PC03-2 | 5 |
| 12 | Orange [L2-P3] | PC03-2 | 3 |  | 12 | Orange [L2-P3] | PC03-2 | 5 |
| 11 | Green [L4-P4] | PC03-2 | 3 |  | 11 | Green [L4-P4] | PC03-2 | 5 |
| 10 | Green [L9-P10] | PC03-2 | 2 |  | 10 | Green [L9-P10] | PC03-2 | 4 |
| 07 | Red [L0-P1] | PC03-2 | 3 |  | 07 | Red [L0-P1] | PC03-2 | 5 |
| 06 | Red [L5-P6] | PC03-2 | 2 |  | 06 | Red [L5-P6] | PC03-2 | 4 |
| 05 | Blue [L7-P7] | PC03-2 | 2 |  | 05 | Blue [L7-P7] | PC03-2 | 4 |
| 04 | Yellow [L6-P8] | PC03-2 | 2 |  | 04 | Yellow [L6-P8] | PC03-2 | 4 |
| 03 | Purple [L3-P5] | PC03-2 | 2 |  | 03 | Purple [L3-P5] | PC03-2 | 4 |
| 02 | Orange [L2-P3] | PC03-2 | 2 |  | 02 | Orange [L2-P3] | PC03-2 | 4 |
| 01 | Green [L4-P4] | PC03-2 | 2 |  | 01 | Green [L4-P4] | PC03-2 | 4 |
| 00 | Green [L9-P10] | PC03-3 | 21 |  | 00 | Green [L9-P10] | PC03-2 | 3 |

Table 13.40, Slot#12 and Slot#13 (Supersector#1).

| Slot# 14 | MB# 1 | Supersector# 2 |  |  | Slot# 15 | MB# 2 | Supersector# 2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-2 | 8 |  | 17 | Red [L0-P1] | PC03-2 | 10 |
| 16 | Red [L5-P6] | PC03-2 | 7 |  | 16 | Red [L5-P6] | PC03-2 | 9 |
| 15 | Blue [L7-P7] | PC03-2 | 7 |  | 15 | Blue [L7-P7] | PC03-2 | 9 |
| 14 | Yellow [L6-P8] | PC03-2 | 7 |  | 14 | Yellow [L6-P8] | PC03-2 | 9 |
| 13 | Purple [L3-P5] | PC03-2 | 7 |  | 13 | Purple [L3-P5] | PC03-2 | 9 |
| 12 | Orange [L2-P3] | PC03-2 | 7 |  | 12 | Orange [L2-P3] | PC03-2 | 9 |
| 11 | Green [L4-P4] | PC03-2 | 7 |  | 11 | Green [L4-P4] | PC03-2 | 9 |
| 10 | Green [L9-P10] | PC03-2 | 6 |  | 10 | Green [L9-P10] | PC03-2 | 8 |
| 07 | Red [L0-P1] | PC03-2 | 7 |  | 07 | Red [L0-P1] | PC03-2 | 9 |
| 06 | Red [L5-P6] | PC03-2 | 6 |  | 06 | Red [L5-P6] | PC03-2 | 8 |
| 05 | Blue [L7-P7] | PC03-2 | 6 |  | 05 | Blue [L7-P7] | PC03-2 | 8 |
| 04 | Yellow [L6-P8] | PC03-2 | 6 |  | 04 | Yellow [L6-P8] | PC03-2 | 8 |
| 03 | Purple [L3-P5] | PC03-2 | 6 |  | 03 | Purple [L3-P5] | PC03-2 | 8 |
| 02 | Orange [L2-P3] | PC03-2 | 6 |  | 02 | Orange [L2-P3] | PC03-2 | 8 |
| 01 | Green [L4-P4] | PC03-2 | 6 |  | 01 | Green [L4-P4] | PC03-2 | 8 |
| 00 | Green [L9-P10] | PC03-2 | 5 |  | 00 | Green [L9-P10] | PC03-2 | 7 |

Table 13.41, Slot#14 and Slot#15 (Supersector#2).

| Slot# 16 | MB# 3 | Supersector# 2 |  |  | Slot# 17 | MB# 4 | Supersector# 2 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-2 | 12 |  | 17 | Red [L0-P1] | PC03-2 | 14 |
| 16 | Red [L5-P6] | PC03-2 | 11 |  | 16 | Red [L5-P6] | PC03-2 | 13 |
| 15 | Blue [L7-P7] | PC03-2 | 11 |  | 15 | Blue [L7-P7] | PC03-2 | 13 |
| 14 | Yellow [L6-P8] | PC03-2 | 11 |  | 14 | Yellow [L6-P8] | PC03-2 | 13 |
| 13 | Purple [L3-P5] | PC03-2 | 11 |  | 13 | Purple [L3-P5] | PC03-2 | 13 |
| 12 | Orange [L2-P3] | PC03-2 | 11 |  | 12 | Orange [L2-P3] | PC03-2 | 13 |
| 11 | Green [L4-P4] | PC03-2 | 11 |  | 11 | Green [L4-P4] | PC03-2 | 13 |
| 10 | Green [L9-P10] | PC03-2 | 10 |  | 10 | Green [L9-P10] | PC03-2 | 12 |
| 07 | Red [L0-P1] | PC03-2 | 11 |  | 07 | Red [L0-P1] | PC03-2 | 13 |
| 06 | Red [L5-P6] | PC03-2 | 10 |  | 06 | Red [L5-P6] | PC03-2 | 12 |
| 05 | Blue [L7-P7] | PC03-2 | 10 |  | 05 | Blue [L7-P7] | PC03-2 | 12 |
| 04 | Yellow [L6-P8] | PC03-2 | 10 |  | 04 | Yellow [L6-P8] | PC03-2 | 12 |
| 03 | Purple [L3-P5] | PC03-2 | 10 |  | 03 | Purple [L3-P5] | PC03-2 | 12 |
| 02 | Orange [L2-P3] | PC03-2 | 10 |  | 02 | Orange [L2-P3] | PC03-2 | 12 |
| 01 | Green [L4-P4] | PC03-2 | 10 |  | 01 | Green [L4-P4] | PC03-2 | 12 |
| 00 | Green [L9-P10] | PC03-2 | 9 |  | 00 | Green [L9-P10] | PC03-2 | 11 |

Table 13.42, Slot#16 and Slot#17 (Supersector#2).

| Slot# 18 | MB# 1 | Supersector# 3 |  |  | Slot# 19 | MB# 2 | Supersector# 3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-2 | 16 |  | 17 | Red [L0-P1] | PC03-2 | 18 |
| 16 | Red [L5-P6] | PC03-2 | 15 |  | 16 | Red [L5-P6] | PC03-2 | 17 |
| 15 | Blue [L7-P7] | PC03-2 | 15 |  | 15 | Blue [L7-P7] | PC03-2 | 17 |
| 14 | Yellow [L6-P8] | PC03-2 | 15 |  | 14 | Yellow [L6-P8] | PC03-2 | 17 |
| 13 | Purple [L3-P5] | PC03-2 | 15 |  | 13 | Purple [L3-P5] | PC03-2 | 17 |
| 12 | Orange [L2-P3] | PC03-2 | 15 |  | 12 | Orange [L2-P3] | PC03-2 | 17 |
| 11 | Green [L4-P4] | PC03-2 | 15 |  | 11 | Green [L4-P4] | PC03-2 | 17 |
| 10 | Green [L9-P10] | PC03-2 | 14 |  | 10 | Green [L9-P10] | PC03-2 | 16 |
| 07 | Red [L0-P1] | PC03-2 | 15 |  | 07 | Red [L0-P1] | PC03-2 | 17 |
| 06 | Red [L5-P6] | PC03-2 | 14 |  | 06 | Red [L5-P6] | PC03-2 | 16 |
| 05 | Blue [L7-P7] | PC03-2 | 14 |  | 05 | Blue [L7-P7] | PC03-2 | 16 |
| 04 | Yellow [L6-P8] | PC03-2 | 14 |  | 04 | Yellow [L6-P8] | PC03-2 | 16 |
| 03 | Purple [L3-P5] | PC03-2 | 14 |  | 03 | Purple [L3-P5] | PC03-2 | 16 |
| 02 | Orange [L2-P3] | PC03-2 | 14 |  | 02 | Orange [L2-P3] | PC03-2 | 16 |
| 01 | Green [L4-P4] | PC03-2 | 14 |  | 01 | Green [L4-P4] | PC03-2 | 16 |
| 00 | Green [L9-P10] | PC03-2 | 13 |  | 00 | Green [L9-P10] | PC03-2 | 15 |

Table 13.43, Slot#18 and Slot#19 (Supersector#3).

| Slot# 20 | MB# 3 | Supersector# 3 |  |  | Slot# 21 | MB# 4 | Supersector# 3 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |  | Mixer Link# | Color [DFE Link#, Port#] | DFE Subrack | DFE Slot |
| 17 | Red [L0-P1] | PC03-2 | 20 |  | 17 | Red [L0-P1] | PC03-3 | 2 |
| 16 | Red [L5-P6] | PC03-2 | 19 |  | 16 | Red [L5-P6] | PC03-2 | 21 |
| 15 | Blue [L7-P7] | PC03-2 | 19 |  | 15 | Blue [L7-P7] | PC03-2 | 21 |
| 14 | Yellow [L6-P8] | PC03-2 | 19 |  | 14 | Yellow [L6-P8] | PC03-2 | 21 |
| 13 | Purple [L3-P5] | PC03-2 | 19 |  | 13 | Purple [L3-P5] | PC03-2 | 21 |
| 12 | Orange [L2-P3] | PC03-2 | 19 |  | 12 | Orange [L2-P3] | PC03-2 | 21 |
| 11 | Green [L4-P4] | PC03-2 | 19 |  | 11 | Green [L4-P4] | PC03-2 | 21 |
| 10 | Green [L9-P10] | PC03-2 | 18 |  | 10 | Green [L9-P10] | PC03-2 | 20 |
| 07 | Red [L0-P1] | PC03-2 | 19 |  | 07 | Red [L0-P1] | PC03-2 | 21 |
| 06 | Red [L5-P6] | PC03-2 | 18 |  | 06 | Red [L5-P6] | PC03-2 | 20 |
| 05 | Blue [L7-P7] | PC03-2 | 18 |  | 05 | Blue [L7-P7] | PC03-2 | 20 |
| 04 | Yellow [L6-P8] | PC03-2 | 18 |  | 04 | Yellow [L6-P8] | PC03-2 | 20 |
| 03 | Purple [L3-P5] | PC03-2 | 18 |  | 03 | Purple [L3-P5] | PC03-2 | 20 |
| 02 | Orange [L2-P3] | PC03-2 | 18 |  | 02 | Orange [L2-P3] | PC03-2 | 20 |
| 01 | Green [L4-P4] | PC03-2 | 18 |  | 01 | Green [L4-P4] | PC03-2 | 20 |
| 00 | Green [L9-P10] | PC03-2 | 17 |  | 00 | Green [L9-P10] | PC03-2 | 19 |

Table 13.44, Slot#20 and Slot#21 (Supersector#3).

# Appendix H – Subrack Controller

## Subrack Controller

Most of the subrack controller information is derived from [Ref. 5].

The Digital Front End Controller (DFEC) sits in slot 1 of the DFE and Mixer subracks, and is responsible for downloading device configuration data files to DFE motherboards and Mixer boards. Additionally, the DFEC monitors the status of the boards in the subrack and makes this data available (via a 1553 interface) to the DZERO slow monitoring system.

The primary function of the DFEC is to quickly download configuration data to the devices on the DFE motherboards and Mixer boards.

Each subrack hosts 20 boards, and each board can have up to 16 devices. Furthermore, the firmware in each of the devices may be unique, thus the controller must be able to manage configuration files for up to 320 devices. For diagnostic reasons, the DFEC board includes enough non-volatile memory (CompactFlash™ card) so that at least two configuration files for each device can be stored locally. The Mixer subrack requires a 128MB or 64MB CompactFlash™ card.

The DFEC uses MSDOS FAT16 file system, allowing for easy file transfers directly to and from the CompactFlash™ card using a commercially available card reader. Files can also be accessed over the 1553 network once the DFEC is installed on the D0 detector platform.

Communications between the Mixer and DFE subracks and the outside world occur through a 1553 interface. The DFEC appears on the 1553 network as a single Remote Terminal (RT). The 1553 bus master can read and write to a small dual port memory located on the DFEC. Using a dual port memory allows for greater decoupling between the 1553 protocol timing and the DFEC microcontroller.

Essentially the DFEC microcontroller acts as a command processor. The 1553 master writes commands and data into the dual port memory, and then generates an interrupt on the microcontroller. The microcontroller wakes up, executes the command(s) and then goes back to idle [Ref. 5d].

Basic status information is read from the Mixer and DFE boards over a dedicated slow monitoring serial bus. This information is continually being collected on the DFEC and made available to the 1553 host. The information collected from the mixer system boards is described in paragraph 4.6.

The DFEC communicates with the Mixer boards over a simple 16-bit address 8-bit data bus (Paragraph 4.5). This bus is not VME compatible.

An Atmel ATMEGA103 is used on the DFEC. It is flash based and supports in-system programmability and contains a debugger that allows the user to step through the code one instruction at a time and set breakpoints, etc. The microcontroller on the DFEC runs off of a 6MHz clock.

Figure 14.1, Subrack controller simplified block diagram

Figure 14.2, Subrack Controller (DFEC) Status Word.

## CompactFlash™ card

The subrack controller uses a CompactFlash™ [Ref. 37] memory card to store the files needed for configuration of the mixer board FPGAs. The FPGA's configuration files are listed in Table 5.1. The memory card also stores up to ten files containing the sequence of commands to be executed by the subrack controller at power-up. Each command file can contains a maximum of 127 bytes, which match the length of the subrack controller command buffer.

The command files are numbered sequentially in the same order they will be executed; their filenames must be "autoexec.000" to "autoexec.009". The subrack controller will stop after executing "autoexec.009" or when the next command file in the sequence is not found.

Figure 14.3, CompactFlash card.

### General information about Compact Flash cards [Ref. 15]

CompactFlash™ is a small removable mass storage device. First introduced in 1994 by SanDisk Corporation [Ref. 37], CF™ cards weigh a half-ounce and are the size of a matchbook (43mm [1.7"] x 36mm [1.4"] x 3.3mm [0.13"]).

CompactFlash cards are designed with flash technology, a non-volatile storage solution that does not require a battery to retain data indefinitely. CompactFlash storage products are solid state, meaning they contain no moving parts.

Dual 3.3V & 5V Operation – CompactFlash cards support both 3.3V and 5V operation and can be interchanged between 3.3V and 5V systems.

Shock – CF cards have an operating shock rating of 2,000 Gs, which is equivalent to a 10-foot drop. With typical usage, a CF card can be used for more than 100 years with no loss or deterioration of data.

Data Reliability – CompactFlash data is protected by built-in dynamic defect management and error correction technologies.

The CompactFlash card can be read/written with the SanDisk ImageMate™ external flash card reader that connects to a computer through a USB port. Another option is the SanDisk PCMCIA card adapter.

### Standard subrack controller commands (autoexec) files

The following two tables describe the content of the two standard "autoexec" or "command" binary files stored on the CompactFlash card to handle the mixer board FPGAs configuration at power-up. The files have been written using a Hex editor [Ref. 43]. Beside the autoexec files the CompactFlash contains the mixer board FPGA's configuration files.

Refer to paragraph 14.3 for a list of the subrack controller commands. The complete description of subrack controller is in available [Ref. 5].

| command (0x) | Notes |
| --- | --- |
| 1200 8102 | Write byte 0x00 to backplane, offset 0x81 (subrack broadcasting to relative address 0x01 Device Status/Control register), slot# 02. This command will write to all the Mixer Boards setting the device select pointer to device 0x00. |
| 5300 4202 0200 | Copy file to backplane, offset 0x42 (mixer board # broadcasting to relative address 0x02 Device Configuration Data register), slot# 02. This command will download to Mixer Boards in slot# 02, 06, 10, 14, 18 the Mixer1/device 00 configuration file "0200_PC.bin". |
| 5300 4203 0300 | Copy file to backplane, offset 0x42 (mixer board # broadcasting to relative address 0x02 Device Configuration Data register), slot# 03. This command will download to Mixer Boards in slot# 03, 07, 11, 15, 19 the Mixer2/device 00 configuration file "0300_PC.bin". |
| 5300 4204 0400 | Copy file to backplane, offset 0x42, slot# 04. This command will download to Mixer Boards in slot# 04, 08, 12, 16, 20 the Mixer3/device 00 configuration file "0400_PC.bin". |
| 5300 4205 0500 | Copy file to backplane, offset 0x42, slot# 05. This command will download to Mixer Boards in slot# 05, 09, 13, 17, 21 the Mixer4/device 00 configuration file "0400_PC.bin". |
| 1201 8102 | Write byte 0x01 to backplane, offset 0x81 (subrack broadcasting to relative address 0x01 Device Status/Control register), slot# 02. This command will write to all the Mixer Boards setting the device select pointer to device 0x01. |
| 5300 4202 0201 | Copy file to backplane, Mixer1/device 01 configuration file "0201_PC.bin". |
| 5300 4203 0301 | Copy file to backplane, Mixer2/device 01 configuration file "0301_PC.bin". |
| 5300 4204 0401 | Copy file to backplane, Mixer3/device 01 configuration file "0401_PC.bin". |
| 5300 4205 0501 | Copy file to backplane, Mixer4/device 01 configuration file "0501_PC.bin". |
| 1202 8102 | Write byte 0x02 to backplane. Sets the device select pointer to device 0x02 in all mixer boards. |
| 5300 4202 0202 | Copy file to backplane, Mixer1/device 02 configuration file "0202_PC.bin". |
| 5300 4203 0302 | Copy file to backplane, Mixer2/device 02 configuration file "0302_PC.bin". |
| 5300 4204 0402 | Copy file to backplane, Mixer3/device 02 configuration file "0402_PC.bin". |
| 5300 4205 0502 | Copy file to backplane, Mixer4/device 02 configuration file "0502_PC.bin". |
| 1203 8102 | Write byte 0x03 to backplane. Sets the device select pointer to device 0x03 in all mixer boards. |
| 5300 4202 0203 | Copy file to backplane, Mixer1/device 03 configuration file "0203_PC.bin". |
| 5300 4203 0303 | Copy file to backplane, Mixer2/device 03 configuration file "0303_PC.bin". |
| 5300 4204 0403 | Copy file to backplane, Mixer3/device 03 configuration file "0403_PC.bin". |
| 5300 4205 0503 | Copy file to backplane, Mixer4/device 03 configuration file "0503_PC.bin". |
| 1204 8102 | Write byte 0x04 to backplane. Sets the device select pointer to device 0x04 in all mixer boards. |
| 5300 4202 0204 | Copy file to backplane, Mixer1/device 04 configuration file "0204_PC.bin". |
| 5300 4203 0304 | Copy file to backplane, Mixer2/device 04 configuration file "0304_PC.bin". |
| 5300 4204 0404 | Copy file to backplane, Mixer3/device 04 configuration file "0404_PC.bin". |
| 5300 4205 0504 | Copy file to backplane, Mixer4/device 04 configuration file "0504_PC.bin". |
| 1205 8102 | Write byte 0x05 to backplane. Sets the device select pointer to device 0x05 in all mixer boards. |
| 5300 4202 0205 | Copy file to backplane, Mixer1/device 05 configuration file "0205_PC.bin". |
| 5300 4203 0305 | Copy file to backplane, Mixer2/device 05 configuration file "0305_PC.bin". |
| 5300 4204 0405 | Copy file to backplane, Mixer3/device 05 configuration file "0405_PC.bin". |
| 5300 4205 0505 | Copy file to backplane, Mixer4/device 05 configuration file "0505_PC.bin". |
| 1206 8102 | Write byte 0x06 to backplane. Sets the device select pointer to device 0x06 in all mixer boards. |
| 5300 4202 0206 | Copy file to backplane, Mixer1/device 06 configuration file "0206_PC.bin". |
| 5300 4203 0306 | Copy file to backplane, Mixer2/device 06 configuration file "0306_PC.bin". |
| 5300 4204 0406 | Copy file to backplane, Mixer3/device 06 configuration file "0406_PC.bin". |
| 5300 4205 0506 | Copy file to backplane, Mixer4/device 06 configuration file "0506_PC.bin". |
| 1207 8102 | Write byte 0x07 to backplane. Sets the device select pointer to device 0x07 in all mixer boards. |
| 5300 4202 0207 | Copy file to backplane, Mixer1/device 07 configuration file "0207_PC.bin". |
| 5300 4203 0307 | Copy file to backplane, Mixer2/device 07 configuration file "0307_PC.bin". |
| 5300 4204 0407 | Copy file to backplane, Mixer3/device 07 configuration file "0407_PC.bin". |
| 5300 4205 0507 | Copy file to backplane, Mixer4/device 07 configuration file "0507_PC.bin". |
| A100 | End of list command. Stop the subrack controller execution of the commands in the command buffer and make him look for next autoexec file. |

Table 14.1, content of file "autoexec.000".

| command (0x) | Notes |
| --- | --- |
| 1208 8102 | Write byte 0x08 to backplane. Sets the device select pointer to device 0x08 in all mixer boards. |
| 5300 4202 0208 | Copy file to backplane, Mixer1/device 08 configuration file "0208_PC.bin". |
| 5300 4203 0308 | Copy file to backplane, Mixer2/device 08 configuration file "0308_PC.bin". |
| 5300 4204 0408 | Copy file to backplane, Mixer3/device 08 configuration file "0408_PC.bin". |
| 5300 4205 0508 | Copy file to backplane, Mixer4/device 08 configuration file "0508_PC.bin". |
| 1209 8102 | Write byte 0x09 to backplane. Sets the device select pointer to device 0x09 in all mixer boards. |
| 5300 4202 0209 | Copy file to backplane, Mixer1/device 09 configuration file "0209_PC.bin". |
| 5300 4203 0309 | Copy file to backplane, Mixer2/device 09 configuration file "0309_PC.bin". |
| 5300 4204 0409 | Copy file to backplane, Mixer3/device 09 configuration file "0409_PC.bin". |
| 5300 4205 0509 | Copy file to backplane, Mixer4/device 09 configuration file "0509_PC.bin". |
| 120A 8102 | Write byte 0x0A to backplane. Sets the device select pointer to device 0x0A in all mixer boards. |
| 5300 4202 020A | Copy file to backplane, Mixer1/device 0A configuration file "020A_PC.bin". |
| 5300 4203 030A | Copy file to backplane, Mixer2/device 0A configuration file "030A_PC.bin". |
| 5300 4204 040A | Copy file to backplane, Mixer3/device 0A configuration file "040A_PC.bin". |
| 5300 4205 050A | Copy file to backplane, Mixer4/device 0A configuration file "050A_PC.bin". |
| 120B 8102 | Write byte 0x0B to backplane. Sets the device select pointer to device 0x0B in all mixer boards. |
| 5300 4202 020B | Copy file to backplane, Mixer1/device 0B configuration file "020B_PC.bin". |
| 5300 4203 030B | Copy file to backplane, Mixer2/device 0B configuration file "030B_PC.bin". |
| 5300 4204 040B | Copy file to backplane, Mixer3/device 0B configuration file "040B_PC.bin". |
| 5300 4205 050B | Copy file to backplane, Mixer4/device 0B configuration file "050B_PC.bin". |
| 120C 8102 | Write byte 0x0C to backplane. Sets the device select pointer to device 0x0C in all mixer boards. |
| 5300 4202 020C | Copy file to backplane, Mixer1/device 0C configuration file "020C_PC.bin". |
| 5300 4203 030C | Copy file to backplane, Mixer2/device 0C configuration file "030C_PC.bin". |
| 5300 4204 040C | Copy file to backplane, Mixer3/device 0C configuration file "040C_PC.bin". |
| 5300 4205 050C | Copy file to backplane, Mixer4/device 0C configuration file "050C_PC.bin". |
| 120D 8102 | Write byte 0x0D to backplane. Sets the device select pointer to device 0x0D in all mixer boards. |
| 5300 4202 020D | Copy file to backplane, Mixer1/device 0D configuration file "020D_PC.bin". |
| 5300 4203 030D | Copy file to backplane, Mixer2/device 0D configuration file "030D_PC.bin". |
| 5300 4204 040D | Copy file to backplane, Mixer3/device 0D configuration file "040D_PC.bin". |
| 5300 4205 050D | Copy file to backplane, Mixer4/device 0D configuration file "050D_PC.bin". |
| 120E 8102 | Write byte 0x0E to backplane. Sets the device select pointer to device 0x0E in all mixer boards. |
| 5300 4202 020E | Copy file to backplane, Mixer1/device 0E configuration file "020E_PC.bin". |
| 5300 4203 030E | Copy file to backplane, Mixer2/device 0E configuration file "030E_PC.bin". |
| 5300 4204 040E | Copy file to backplane, Mixer3/device 0E configuration file "040E_PC.bin". |
| 5300 4205 050E | Copy file to backplane, Mixer4/device 0E configuration file "050E_PC.bin". |
| 120F 8102 | Write byte 0x0F to backplane. Sets the device select pointer to device 0x0F in all mixer boards. |
| 5300 4202 020F | Copy file to backplane, Mixer1/device 0F configuration file "020F_PC.bin". |
| 5300 4203 030F | Copy file to backplane, Mixer2/device 0F configuration file "030F_PC.bin". |
| 5300 4204 040F | Copy file to backplane, Mixer3/device 0F configuration file "040F_PC.bin". |
| 5300 4205 050F | Copy file to backplane, Mixer4/device 0F configuration file "050F_PC.bin". |
| A100 | End of list command. Stop the subrack controller execution of the commands in the command buffer and make him look for next autoexec file. |

Table 14.2, content of file "autoexec.001".

## Subrack Controller Commands

The following tables provide the list of the subrack controller commands. For complete documentation refer to [Ref. 5].

| Write Byte to Backplane |  | Read Byte from Backplane |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit# | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0x1 | 0x2 | data byte | 1stword | 0x2 | 0x2 |  |
| offset |  | slot number | 2ndword | offset |  | slot number |

| CompactFlash to Sector Buffer |  | SectorBuffer toCompactFlash |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0x3 | 0x2 | lba high byte | 1stword | 0x4 | 0x2 | lba high byte |
| lba mid byte | lba low byte | 2ndword | lba mid byte | lba low byte |

| Copy File to Backplane |  | Delete File from CompactFlash |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0x5 | 0x3 |  | 1stword | 0x9 | 0x2 |  |
| offset |  | slot number | 2ndword | file name |
| file name | 3rd word |  |  |

| Append Sector to File |  | Generate File Checksum |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0x8 | 0x2 |  | 1stword | 0x7 | 0x2 |  |
| file name | 2ndword | file name |

| Reset Board |  | Set Clock Bits |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0x7 | 0x1 |  | slot number | 1stword | 0xC | 0x1 |  | clk | slot number |

| Configure Device |  | Get Firmware Revision |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0x6 | 0x3 |  | slot number | 1stword | 0xB | 0x2 |  | slot number |
|  | device # | firmware rev byte | 2ndword |  | device # |  |
| file name | 3rdword |  |  |

| NOP Command |  | Get File Size |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # | F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| 0xF | 0x1 |  | 1stword | 0xD | 0x2 |  |
|  | 2ndword | file name |

| End of List |  |  |
| --- | --- | --- |
| F | E | D | C | B | A | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | bit # |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0xA | 0x1 | 0x0 | 1stword |  |  |  |

### Examples of command usage

| command (0x) | Notes |
| --- | --- |
| 1202 0015 | Write 0x02 to the Board Status/Control register of mixer board in slot# 21 (0x15). This operation will force the board in the reset state. The FPGAs configuration will be retained. |
| 1200 0015 | Write 0x00 to the Board Status/Control register of mixer board in slot# 21 (0x15). The mixer board will be forced out of the reset state and resume normal operations. |

Table 14.3, Example of mixer board reset operation.

| command (0x) | Notes |
| --- | --- |
| 1200 8B0C | Write 0x00 to the Monitoring Mode register of all mixer boards. This operation will change the LED monitoring mode to mode#0 (input links clock and DLL status). |

Table 14.4, Example of change LED monitoring mode operation.

| command (0x) | Notes |
| --- | --- |
| 1217 2409 | Write 0x17 to the Mode of Operation register (address 0x04) of the boards in the second mixer subsystem (slot# 6, 7, 8, 9). This operation enables the "Device Access Registers", allowing to access registers located on mixer board FPGAs. |
| 120A 2109 | Write 0x0A to the Device Status/Control register (address 0x01) of the boards in the second mixer subsystem (slot# 6, 7, 8, 9). This operation point the board controller to talk to device# 0A (IN0 FPGA) |
| 12<reg> 2709 | Write <reg> to the Device Access Address register (address 0x07) of the boards in the second mixer subsystem (slot# 6, 7, 8, 9). This operation point the board controller to talk to the specific register address <reg> inside the device specified in the previous operation. If the LED monitoring mode is set to mode 8 the front panel LEDs 0..7 will display the content of the local bus that is continuously driven by the content of the register <reg> of device #0A. |
| 2200 0806 | Readback the content of the Device Access Data register on the mixer board in slot #6. The byte read is the content of register <reg> inside device# 0A. |
| 12<data_byte> 0806 | Write <data_byte> to the Device Access Data register on the mixer board in slot #6. This operation will write the <data_byte> to the register <reg> of device #0A. |

Table 14.5, Example of device access operations.

## Test procedures information

A separate document provides [Ref. 8c] information on mixer board/system test procedures.

## Diagnostic procedures information

A separate document provides [Ref. 8d] information and examples on mixer system diagnostic procedures.

# Appendix I – CPS re-mapping conversion tables

The following 4 four tables provide the re-mapping information for the CPS data bits received by the mixer system. The original CPS data stream was sent to each mixer board over a 28 bit wide links (one of the 28 bits is used for frame synchronization). The new CPS data stream will be sent over a 21 bit wide data stream (one of the 21 bits used for frame synchronization). The original data stream had a total of 128 data bits per frame (seven clock cycles), the new one has only 64 data bits per frame.

Data bits marked as "X" (blue background color) are lost due to 28 to 21 bits re-mapping.

Data bits marked as "S" (gray background color) are still handled by the mixer but will not be used by the AFEs to send data and will be ignored by the DFEs.

| Re-mapping of the CPS link data bits sent to Mixer 1 |
| --- |
| old designation | new designation | old designation | new designation | old designation | new designation | old designation | new designation |
| CPSL1 | CPS1 | CPSL33 | CPS33 | CPSH1 | CPS6 | CPSH33 | S |
| CPSL2 | CPS2 | CPSL34 | CPS34 | CPSH2 | CPS7 | CPSH34 | CPS41 |
| CPSL3 | CPS3 | CPSL35 | CPS35 | CPSH3 | CPS8 | CPSH35 | S |
| CPSL4 | CPS4 | CPSL36 | CPS36 | CPSH4 | CPS9 | CPSH36 | CPS43 |
| CPSL5 | S | CPSL37 | CPS37 | CPSH5 | CPS10 | CPSH37 | S |
| CPSL6 | CPS5 | CPSL38 | CPS38 | CPSH6 | S | CPSH38 | CPS40 |
| CPSL7 | S | CPSL39 | CPS39 | CPSH7 | S | CPSH39 | CPS42 |
| CPSL8 | S | CPSL40 | S | CPSH8 | X | CPSH40 | X |
| CPSL9 | CPS11 | CPSL41 | X | CPSH9 | X | CPSH41 | CPS44 |
| CPSL10 | CPS12 | CPSL42 | X | CPSH10 | X | CPSH42 | CPS45 |
| CPSL11 | CPS13 | CPSL43 | X | CPSH11 | X | CPSH43 | CPS46 |
| CPSL12 | CPS14 | CPSL44 | X | CPSH12 | X | CPSH44 | CPS47 |
| CPSL13 | CPS15 | CPSL45 | X | CPSH13 | X | CPSH45 | CPS48 |
| CPSL14 | CPS16 | CPSL46 | X | CPSH14 | X | CPSH46 | CPS49 |
| CPSL15 | S | CPSL47 | X | CPSH15 | X | CPSH47 | CPS50 |
| CPSL16 | S | CPSL48 | X | CPSH16 | S | CPSH48 | S |
| CPSL17 | CPS17 | CPSL49 | X | CPSH17 | S | CPSH49 | CPS51 |
| CPSL18 | S | CPSL50 | X | CPSH18 | CPS21 | CPSH50 | CPS52 |
| CPSL19 | CPS18 | CPSL51 | X | CPSH19 | S | CPSH51 | CPS53 |
| CPSL20 | CPS19 | CPSL52 | X | CPSH20 | S | CPSH52 | S |
| CPSL21 | S | CPSL53 | X | CPSH21 | CPS22 | CPSH53 | S |
| CPSL22 | CPS20 | CPSL54 | X | CPSH22 | S | CPSH54 | CPS54 |
| CPSL23 | X | CPSL55 | S | CPSH23 | S | CPSH55 | S |
| CPSL24 | X | CPSL56 | S | CPSH24 | S | CPSH56 | S |
| CPSL25 | CPS23 | CPSL57 | CPS55 | CPSH25 | S | CPSH57 | CPS62 |
| CPSL26 | CPS24 | CPSL58 | CPS56 | CPSH26 | S | CPSH58 | CPS63 |
| CPSL27 | CPS25 | CPSL59 | CPS57 | CPSH27 | S | CPSH59 | S |
| CPSL28 | CPS26 | CPSL60 | CPS58 | CPSH28 | S | CPSH60 | CPS64 |
| CPSL29 | CPS27 | CPSL61 | CPS59 | CPSH29 | CPS30 | CPSH61 | S |
| CPSL30 | CPS28 | CPSL62 | CPS60 | CPSH30 | CPS31 | CPSH62 | X |
| CPSL31 | CPS29 | CPSL63 | CPS61 | CPSH31 | CPS32 | CPSH63 | X |
| CPSL32 | S | CPSL64 | S | CPSH32 | S | CPSH64 | X |

Table 15.1, Mixer 1 CPS data bits re-mapping.

| Re-mapping of the CPS link data bits sent to Mixer 2 |
| --- |
| old designation | new designation | old designation | new designation | old designation | new designation | old designation | new designation |
| CPSL65 | CPS65 | CPSL97 | CPS97 | CPSH65 | CPS70 | CPSH97 | S |
| CPSL66 | CPS66 | CPSL98 | CPS98 | CPSH66 | CPS71 | CPSH98 | CPS105 |
| CPSL67 | CPS67 | CPSL99 | CPS99 | CPSH67 | CPS72 | CPSH99 | S |
| CPSL68 | CPS68 | CPSL100 | CPS100 | CPSH68 | CPS73 | CPSH100 | CPS107 |
| CPSL69 | S | CPSL101 | CPS101 | CPSH69 | CPS74 | CPSH101 | S |
| CPSL70 | CPS69 | CPSL102 | CPS102 | CPSH70 | S | CPSH102 | CPS104 |
| CPSL71 | S | CPSL103 | CPS103 | CPSH71 | S | CPSH103 | CPS106 |
| CPSL72 | S | CPSL104 | S | CPSH72 | X | CPSH104 | X |
| CPSL73 | CPS75 | CPSL105 | X | CPSH73 | X | CPSH105 | CPS108 |
| CPSL74 | CPS76 | CPSL106 | X | CPSH74 | X | CPSH106 | CPS109 |
| CPSL75 | CPS77 | CPSL107 | X | CPSH75 | X | CPSH107 | CPS110 |
| CPSL76 | CPS78 | CPSL108 | X | CPSH76 | X | CPSH108 | CPS111 |
| CPSL77 | CPS79 | CPSL109 | X | CPSH77 | X | CPSH109 | CPS112 |
| CPSL78 | CPS80 | CPSL110 | X | CPSH78 | X | CPSH110 | CPS113 |
| CPSL79 | S | CPSL111 | X | CPSH79 | X | CPSH111 | CPS114 |
| CPSL80 | S | CPSL112 | X | CPSH80 | S | CPSH112 | S |
| CPSL81 | CPS81 | CPSL113 | X | CPSH81 | CPS85 | CPSH113 | CPS115 |
| CPSL82 | S | CPSL114 | X | CPSH82 | S | CPSH114 | S |
| CPSL83 | CPS82 | CPSL115 | X | CPSH83 | S | CPSH115 | CPS116 |
| CPSL84 | CPS83 | CPSL116 | X | CPSH84 | S | CPSH116 | CPS117 |
| CPSL85 | S | CPSL117 | X | CPSH85 | CPS86 | CPSH117 | S |
| CPSL86 | CPS84 | CPSL118 | X | CPSH86 | S | CPSH118 | CPS118 |
| CPSL87 | X | CPSL119 | S | CPSH87 | S | CPSH119 | S |
| CPSL88 | X | CPSL120 | S | CPSH88 | S | CPSH120 | S |
| CPSL89 | CPS87 | CPSL121 | CPS119 | CPSH89 | S | CPSH121 | CPS126 |
| CPSL90 | CPS88 | CPSL122 | CPS120 | CPSH90 | S | CPSH122 | S |
| CPSL91 | CPS89 | CPSL123 | CPS121 | CPSH91 | S | CPSH123 | CPS127 |
| CPSL92 | CPS90 | CPSL124 | CPS122 | CPSH92 | S | CPSH124 | CPS128 |
| CPSL93 | CPS91 | CPSL125 | CPS123 | CPSH93 | CPS94 | CPSH125 | S |
| CPSL94 | CPS92 | CPSL126 | CPS124 | CPSH94 | CPS95 | CPSH126 | X |
| CPSL95 | CPS93 | CPSL127 | CPS125 | CPSH95 | CPS96 | CPSH127 | X |
| CPSL96 | S | CPSL128 | S | CPSH96 | S | CPSH128 | X |

Table 15.2, Mixer 2 CPS data bits re-mapping.

| Re-mapping of the CPS link data bits sent to Mixer 3 |
| --- |
| old designation | new designation | old designation | new designation | old designation | new designation | old designation | new designation |
| CPSL129 | CPS129 | CPSL161 | CPS161 | CPSH129 | CPS134 | CPSH161 | S |
| CPSL130 | CPS130 | CPSL162 | CPS162 | CPSH130 | CPS135 | CPSH162 | CPS169 |
| CPSL131 | CPS131 | CPSL163 | CPS163 | CPSH131 | CPS136 | CPSH163 | S |
| CPSL132 | CPS132 | CPSL164 | CPS164 | CPSH132 | CPS137 | CPSH164 | CPS171 |
| CPSL133 | S | CPSL165 | CPS165 | CPSH133 | CPS138 | CPSH165 | S |
| CPSL134 | CPS133 | CPSL166 | CPS166 | CPSH134 | S | CPSH166 | CPS168 |
| CPSL135 | S | CPSL167 | CPS167 | CPSH135 | S | CPSH167 | CPS170 |
| CPSL136 | S | CPSL168 | S | CPSH136 | X | CPSH168 | X |
| CPSL137 | CPS139 | CPSL169 | X | CPSH137 | X | CPSH169 | CPS172 |
| CPSL138 | CPS140 | CPSL170 | X | CPSH138 | X | CPSH170 | CPS173 |
| CPSL139 | CPS141 | CPSL171 | X | CPSH139 | X | CPSH171 | CPS174 |
| CPSL140 | CPS142 | CPSL172 | X | CPSH140 | X | CPSH172 | CPS175 |
| CPSL141 | CPS143 | CPSL173 | X | CPSH141 | X | CPSH173 | CPS176 |
| CPSL142 | CPS144 | CPSL174 | X | CPSH142 | X | CPSH174 | CPS177 |
| CPSL143 | S | CPSL175 | X | CPSH143 | X | CPSH175 | CPS178 |
| CPSL144 | S | CPSL176 | X | CPSH144 | S | CPSH176 | S |
| CPSL145 | CPS145 | CPSL177 | X | CPSH145 | S | CPSH177 | CPS179 |
| CPSL146 | S | CPSL178 | X | CPSH146 | CPS149 | CPSH178 | S |
| CPSL147 | S | CPSL179 | X | CPSH147 | S | CPSH179 | CPS180 |
| CPSL148 | CPS146 | CPSL180 | X | CPSH148 | S | CPSH180 | CPS181 |
| CPSL149 | CPS147 | CPSL181 | X | CPSH149 | CPS150 | CPSH181 | S |
| CPSL150 | CPS148 | CPSL182 | X | CPSH150 | S | CPSH182 | CPS182 |
| CPSL151 | X | CPSL183 | S | CPSH151 | S | CPSH183 | S |
| CPSL152 | X | CPSL184 | S | CPSH152 | S | CPSH184 | S |
| CPSL153 | CPS151 | CPSL185 | CPS183 | CPSH153 | S | CPSH185 | CPS190 |
| CPSL154 | CPS152 | CPSL186 | CPS184 | CPSH154 | S | CPSH186 | S |
| CPSL155 | CPS153 | CPSL187 | CPS185 | CPSH155 | S | CPSH187 | CPS191 |
| CPSL156 | CPS154 | CPSL188 | CPS186 | CPSH156 | S | CPSH188 | S |
| CPSL157 | CPS155 | CPSL189 | CPS187 | CPSH157 | CPS158 | CPSH189 | CPS192 |
| CPSL158 | CPS156 | CPSL190 | CPS188 | CPSH158 | CPS159 | CPSH190 | X |
| CPSL159 | CPS157 | CPSL191 | CPS189 | CPSH159 | CPS160 | CPSH191 | X |
| CPSL160 | S | CPSL192 | S | CPSH160 | S | CPSH192 | X |

Table 15.3, Mixer 3 CPS data bits re-mapping.

| Re-mapping of the CPS link data bits sent to Mixer 4 |
| --- |
| old designation | new designation | old designation | new designation | old designation | new designation | old designation | new designation |
| CPSL193 | CPS193 | CPSL225 | CPS225 | CPSH193 | CPS198 | CPSH225 | S |
| CPSL194 | CPS194 | CPSL226 | CPS226 | CPSH194 | CPS199 | CPSH226 | CPS233 |
| CPSL195 | CPS195 | CPSL227 | CPS227 | CPSH195 | CPS200 | CPSH227 | S |
| CPSL196 | CPS196 | CPSL228 | CPS228 | CPSH196 | CPS201 | CPSH228 | CPS235 |
| CPSL197 | CPS197 | CPSL229 | CPS229 | CPSH197 | CPS202 | CPSH229 | S |
| CPSL198 | S | CPSL230 | CPS230 | CPSH198 | S | CPSH230 | CPS232 |
| CPSL199 | S | CPSL231 | CPS231 | CPSH199 | S | CPSH231 | CPS234 |
| CPSL200 | S | CPSL232 | S | CPSH200 | X | CPSH232 | X |
| CPSL201 | CPS203 | CPSL233 | X | CPSH201 | X | CPSH233 | CPS236 |
| CPSL202 | CPS204 | CPSL234 | X | CPSH202 | X | CPSH234 | CPS237 |
| CPSL203 | CPS205 | CPSL235 | X | CPSH203 | X | CPSH235 | CPS238 |
| CPSL204 | CPS206 | CPSL236 | X | CPSH204 | X | CPSH236 | CPS239 |
| CPSL205 | CPS207 | CPSL237 | X | CPSH205 | X | CPSH237 | CPS240 |
| CPSL206 | CPS208 | CPSL238 | X | CPSH206 | X | CPSH238 | CPS241 |
| CPSL207 | S | CPSL239 | X | CPSH207 | X | CPSH239 | CPS242 |
| CPSL208 | S | CPSL240 | X | CPSH208 | S | CPSH240 | S |
| CPSL209 | CPS209 | CPSL241 | X | CPSH209 | S | CPSH241 | CPS243 |
| CPSL210 | S | CPSL242 | X | CPSH210 | CPS213 | CPSH242 | S |
| CPSL211 | CPS210 | CPSL243 | X | CPSH211 | S | CPSH243 | CPS244 |
| CPSL212 | CPS211 | CPSL244 | X | CPSH212 | S | CPSH244 | CPS245 |
| CPSL213 | S | CPSL245 | X | CPSH213 | CPS214 | CPSH245 | S |
| CPSL214 | CPS212 | CPSL246 | X | CPSH214 | S | CPSH246 | CPS246 |
| CPSL215 | X | CPSL247 | S | CPSH215 | S | CPSH247 | S |
| CPSL216 | X | CPSL248 | S | CPSH216 | S | CPSH248 | S |
| CPSL217 | CPS215 | CPSL249 | CPS247 | CPSH217 | S | CPSH249 | CPS254 |
| CPSL218 | CPS216 | CPSL250 | CPS248 | CPSH218 | S | CPSH250 | S |
| CPSL219 | CPS217 | CPSL251 | CPS249 | CPSH219 | S | CPSH251 | CPS255 |
| CPSL220 | CPS218 | CPSL252 | CPS250 | CPSH220 | S | CPSH252 | S |
| CPSL221 | CPS219 | CPSL253 | CPS251 | CPSH221 | CPS222 | CPSH253 | CPS256 |
| CPSL222 | CPS220 | CPSL254 | CPS252 | CPSH222 | CPS223 | CPSH254 | X |
| CPSL223 | CPS221 | CPSL255 | CPS253 | CPSH223 | CPS224 | CPSH255 | X |
| CPSL224 | S | CPSL256 | S | CPSH224 | S | CPSH256 | X |

Table 15.4, Mixer 4 CPS data bits re-mapping.

# Appendix L - Notes about Input Links swapping

The 20 data bits of each LVDS input Link (excluding the SYNC bit) can be divided in two sets of ten bits, the 10 Least Significative bits and the 10 Most Significative bits. The two sets of bits may have to be swapped (i.e. exchange their position) before any operation of data multiplexing is performed in the backend (backplane FPGAs and backend FPGAs). This swapping depends on the particular link considered and the Mixer Board position inside a supersector (i.e. MB1, 2, 3 or 4). This feature was used to simplify the hardware design and reduce the number of required connections on the Mixer Board. Furthermore it allowed the use of just one hardware design for the 4 different firmware codes used (for Mixer#1, 2, 3, 4).

There is another reason for link swapping. The AFE LHBs (Left Hand Boards) have the top and bottom ten bits of the link swapped from what was the original specification. The link swapping is used to correct this problem. The link swapping is then completely defined by the system of which the mixer system is part of (D0 Central Tracker Trigger). The swapping information embedded in the mixer system firmware is reported in Table 16.1.

|  |  | Link swapping top eight input links | Link swapping bottom eight input links |
| --- | --- | --- | --- |
| Mixer Board# |  | Binary content | Swapped links | Binary content | Swapped links |
|  | Mixer swap only (a) | 11110100 | 15, 14, 13, 12, 10 | 11010000 | 7, 6, 4 |
| 1 | AFE LHB swap only (b) | 10011110 | 15, 12, 11, 10, 9 | 10000110 | 7, 2, 1 |
|  | both Mixer and AFE swaps = (a) XOR (b) | 01101010 (0x6A) | 14, 13, 11, 9 | 01010110 (0x56) | 6, 4, 2, 1 |
|  | Mixer swap only (a) | 10000010 | 15, 9 | 11100010 | 7, 6, 5, 1 |
| 2 | AFE LHB swap only (b) | 10000111 | 15, 10, 9, 8 | 01100100 | 6, 5, 2 |
|  | both Mixer and AFE swaps = (a) XOR (b) | 00000101 (0x05) | 10, 8 | 10000110 (0x86) | 7, 2, 1 |
|  | Mixer swap only (a) | 00100000 | 13 | 11110000 | 7, 6, 5, 4 |
| 3 | AFE LHB swap only (b) | 10110011 | 15, 13, 12, 9, 8 | 01010100 | 6, 4, 2 |
|  | both Mixer and AFE swaps = (a) XOR (b) | 10010011 (0x93) | 15, 12, 9, 8 | 10100100 (0xA4) | 7, 5, 2 |
|  | Mixer swap only (a) | 00000010 | 9 | 11010010 | 7, 6, 4, 1 |
| 4 | AFE LHB swap only (b) | 11010010 | 15, 14, 12, 9 | 10010100 | 7, 4, 2 |
|  | both Mixer and AFE swaps = (a) XOR (b) | 11010000 (0xD0) | 15, 14, 12 | 01000110 (0x46) | 6, 2, 1 |

Table 16.1, Link swapping information.

# Glossary

AFE: acronym for Analog Front-End Board.

Analog Front-End Board (AFE): It has the function of receiving charge signals from the Central Fiber Tracker (CFT) and providing digital hit pattern for those charge signals. The AFEs are located on the VLPC cassette cryostat. More details in Chapter 3 and [Ref. 7].

ANSI: American National Standards Institute. More information is available on the Internet:
http://www.ansi.org/

BIST: Built-In Self Test, the method of designing circuits with additional logic that can be used to test correct operation of the primary (functional) logic.

BSDL: Boundary Scan Description Language. IEEE 1149.1-1993b defines a language that describes IEEE 1149.1 architecture for an integrated circuit. This language is known as the Boundary Scan Description Language (BSDL). Updated BSDL files for the XILINX devices used on the Mixer Board can be found at: http://support.xilinx.com/support/sw_bsdl.htm

Compact Flash card: is a removable mass storage device. The card is designed based on the PC Card (PCMCIA) standard [Ref. 37].

CFT: Central Fiber Tracker.

CPS: Central Pre-Shower.

DFE: Digital Front-End board.

Digital Front-End Board: it has the function of generating the trigger using the data received from the mixer system. More details in Chapter 3 and [Ref. 5].

EDIF: Electronic Data Interchange Format. Industry-standard for specifying a logic design in text (ASCII) form.

EIA: Electronics Industries Alliance. More information is available on the Internet:
http://www.eia.org/

File types:

JEDEC files

JEDEC files are CPLD programming files generated by the CPLD fitter. They are ASCII text files containing programming information and, optionally, functional test vectors that can be used to verify the correct functional behavior of the programmed device. One JEDEC file is required for each device in the JTAG programming chain. The extension for JEDEC files is .jed.

BSDL Summary files

The Boundary-Scan Description Language (BSDL) files use a subset of VHDL to describe the boundary scan features of a device. The Xilinx JTAG Programmer automatically extracts the length of the instruction register from the BSDL file to place non-Xilinx devices in bypass mode. Xilinx BSDL files are located automatically by the JTAG Programmer. The name of the BSDL file is assumed to be <device name>.bsd.

BIT Files

Bit files are Xilinx FPGA configuration files generated by the Xilinx FPGA design software. They are proprietary format binary files containing configuration information. One BIT file is required for each Xilinx FPGA in the JTAG boundary-scan chain. The extension for BIT files is ".bit".

(MCS/EXO) PROM Files

PROM programming files are generated by the Xilinx PROM file formatter. They are ascii text files used to specify configuration data. One PROM file is required for each Xilinx PROM in the JTAG boundary-scan chain. Use the device properties (Edit>Properties) dialog to specify the location of the MCS/EXO files for each Xilinx PROM. The required extensions for MCS and EXO files are ".mcs" and ".exo" respectively.

FPGA: Field Programmable Gate Array. An integrated circuit that contains configurable (programmable) logic blocks and configurable (programmable) interconnect between these blocks.

IEEE: Institute of Electrical and Electronics Engineers, Inc. More information is available on the Internet:
http://www.ieee.org/

Jedec: The JEDEC Solid State Technology Association (once known as the Joint Electron Device Engineering Council), is the semiconductor engineering standardization body of the Electronic Industries Alliance (EIA), a trade association that represents all areas of the electronics industry. More information is available on the Internet:
http://www.jedec.org/

Jitter: The JEDEC Standard No. 65 (EIA/JESD65) defines jitter as the magnitude of the time deviation of a controlled edge from its nominal position.

JTAG: Joint Test Action Group. Older name for IEEE 1149.1 boundary scan, a method to test printed circuit boards and also integrated circuits. See also BSDL.
Design complexity, difficulty of loaded board testing, and the limited pin access of surface mount technology led industry leaders to seek accord on a standard to support the solution of these problems.
The standard defines a hardware architecture and the mechanisms for its use.
The standard itself defines instructions that can be used to perform functional and interconnect tests as well as built-in self test procedures. Vendor-specific extensions to the standard have been developed to allow execution of maintenance and diagnostic applications as well as programming algorithms for re-configurable parts. 
The top level schematic of the test logic defined by IEEE Std 1149.1 includes three key blocks:

The TAP Controller

This responds to the control sequences supplied through the test access port (TAP) and generates the clock and control signals required for correct operation of the other circuit blocks.

The Instruction Register

This shift register-based circuit is serially loaded with the instruction that selects an operation to be performed.

The Data Registers

These are a bank of shift register based circuits. The stimuli required by an operation are serially loaded into the data registers selected by the current instruction. Following execution of the operation, results can be shifted out for examination.

The JTAG Test Access Port (TAP) contains four pins that drive the circuit blocks and control the operations specified. The TAP facilitates the serial loading and unloading of instructions and data. The four pins of the TAP are: TMS (Test Mode Select), TCK (Test Clock), TDI (Test Data In) and TDO (Test Data Out). The function of each TAP pin is as follows:

TCK -	 this pin is the JTAG test clock. It sequences the TAP controller as well as all of the JTAG registers.

TMS -	 this pin is the mode input signal to the TAP Controller. The TAP controller is a FSM that provides the control logic for JTAG. The state of TMS at the rising edge of TCK determines the sequence of states for the TAP controller. TMS has an internal pull-up resistor on it to provide a logic 1 to the system if the pin is not driven.

TDI -	this pin is the serial data input to all JTAG instruction and data registers. The state of the TAP controller as well as the particular instruction held in the instruction register determines which register is fed by TDI for a specific operation. TDI has an internal pull-up resistor on it to provide a logic 1 to the system if the pin is not driven. TDI is sampled into the JTAG registers on the rising edge of TCK.

TDO - 	this pin is the serial data output for all JTAG instruction and data registers. The state of the TAP controller as well as the particular instruction held in the instruction register determines which register feeds TDO for a specific operation. Only one register (instruction or data) is allowed to be the active connection between TDI and TDO for any given operation. TDO changes state on the falling edge of TCK and is only active during the shifting of data through the device. This pin is three-stated at all other times.

LVDS: Low Voltage Differential Signaling, otherwise known as TIA/EIA-644. Is a signaling method used for high-speed, low-power transmission of binary data over copper [Ref. 38].

LVTTL: Low Voltage TTL. Is one of the several switching standards used in digital electronics [Ref. 38].

Figure 17.1, Switching standards.

Figure 17.2, Comparison of switching standards.

MCU: Micro-Controller Unit.

MIL-STD-1553: standard developed to define a serial communications bus to interconnect different subsystems which need to share or exchange information.

SERDES: Serializer/Deserializer. Used to indicate LVDS components using data serialization (also called Data Channel Compression) to reduce the number of physical connection required for a data channel.

Skew: The JEDEC Standard No. 65 (EIA/JESD65) defines skew as The magnitude of the time difference between two events that ideally would occur simultaneously.

VHDL: "V" stands for Very High Speed Integrated Circuit and "HDL" stands for Hardware Description Language.

# References

[1] Paul Horowitz, Winfield Hill, “The Art of Electronics”, 1995, Cambridge University Press. ISBN 0-521-37095-7.

[2] Howard Johnson, Martin Graham, 
“High Speed Digital Design”, 1993, Prentice Hall PTR. ISBN 0-13-395724-1.

[3] Wade D.Peterson, VMEbus International Trade Association, “The VMEbus Handbook”, Fourth edition 1997. ISBN 1-885731-08-6.

[4] Design Specification Master Document for the Electronic Mixing Box System, 
D0 Electronics Group.
Information available on Internet:
http://d0server1.fnal.gov/Projects/TriggerElectronics/WebDocs/MixerBox/doc_indx.html

[5] Jamieson T. Olsen,

  - "Digital Front End Mother Board register map", Engineering Note 2000-01-28a.

  - "DFE and Mixer Board Registers ", Engineering Note 2000-01-28a.

  - "DFE backplane address/data bus protocol", Engineering Note 2000-03-28a.

  - "DFE slow monitoring custom serial bus specification", 
 Engineering Note 2000-01-31a.

  - Digital Front End Controller (DFEc) Board:
http://d0server1.fnal.gov/users/jamieson/www/projects/dfec/index.html

Information available on the internet: http://d0server1.fnal.gov/users/jamieson/www/index.html

[6] Robert D. Angstad, technical documentation.
Information available on the internet:
http://d0server1.fnal.gov/users/angstadt/www/datapump/datapump.htm

[7] John T. Anderson,

- “D-Zero Central Fiber Tracker 8-MCM Analog Front End Board, 
 Design Specification”, January 7, 2000.

Information available on Internet:
http://d0server1.fnal.gov/users/janderson/Public_Eng_Notes/default.html.

[8] Mixer System documentation

- Neal Wilcer, John Anderson, Stefano Rapisarda “Central Tracker Trigger (CTT) Mixer System Backplane Description & Power Distribution Specification”, July 4, 2000. Document#: ESE-D0-000704.

- Makoto Tomoto, "Note on cable mapping from AFE to Mixer", October 26, 2001.

- D0 Mixer System Test Procedures.

- D0 Mixer System Diagnostic Procedures.

The mentioned documents and several others are available on Internet: 
http://www-ese.fnal.gov/D0_CTT_Mixer/

[9] Private communication from undisclosed source.

[10] Private communication from John Smith.

[11] Agilent (formerly Hewlett-Packard) documentation:

- Probing Solutions for Agilent Technologies Logic Analysis Systems.

Information available on Internet:
http://www.agilent.com/

[12] Aldec. Web site: http://www.aldec.com/.

[13] Amp. Web site: http://www.amp.com/.

[14] Brookdale Electronics. Web site: http://www.brookdale.com/ .

[15] Compact Flash Association. Web site: http://www.compactflash.org/

[16] Corel Draw is a drawing software package by Corel. Web site: http://www.corel.com

[17] Corelis Web site: http://www.corelis.com

[18] Cypress. Web site: http://www.cypress.com

[19] C&K. It has been acquired by ITT Industries, Cannon connectors division.
Web site: http://www.ittcannon.com/

[20] Elmec Technology. Web site: http://www.elmectech.com/

[21] ERNI. Web site: http://www.erni.com/

[22] Fairchild. Web site: http://www.fairchildsemi.com/

[23] FPGA Express is an FPGA synthesis software tool by Synopsys. Web site: http://www.synopsys.com/

[24] Harting. Web site: http://www.harting.com/

[25] Hyperlynx is a signal integrity software package by Innoveda. Web site: http://www.innoveda.com/

[26] I-Cube. Web site: http://www.icube.com/

[27] IDT. Web site: http://www.idt.com/

[28] Leonardo Spectrum is an FPGA synthesis software tool by Mentor Graphics. Web site: http://www.mentor.com/

[29] Linear Technology. Web site: http://www.linear-tech.com/

[30] Littlefuse. Web site: http://www.littlefuse.com/

[31] Lumex. Web site: http://www.lumex.com/

[32] Micrel. Web site: http://www.micrel.com/ .

[33] Motorola (semiconductors division). Web site: http://e-www.motorola.com/

[34] National Semiconductors. Web site: http://www.national.com/

[35] ON Semiconductor. Web site: http://www.onsemi.com/

[36] Philips. Web site: http://www.philips.com/

[37] SanDisk documentation. Information available on Internet:
http://www.sandisk.com/

[38] Texas Instrument documentation:

  - Interface Circuits for TIA/EIA-644(LVDS), November 1998, document SLLA038.

  - SN65LVDS93 LVDS SERDES Transmitter, data sheet document SLLS302F.

  - SN65LVDS94 LVDS SERDES Receiver, data sheet document SLLS298E.

  - SN65LVDS95 LVDS SERDES Transmitter, data sheet document SLLS297F.

  - SN65LVDS96 LVDS SERDES Receiver, data sheet document SLLS296F.

  - Comparing Bus Solutions, March 2000, application report document SLLA067.

Information available on Internet: http://www.ti.com/

[39] Vicor. Web site: http://www.vicr.com/

[40] Xilinx documentation:

- Spartan and Spartan-XL Families Field Programmable Gate Arrays, Product Specification, DS060 (v1.5) March 2, 2000 (Data Sheet file: ds060.pdf).

- Data Generation and Configuration for Spartan Spartan Series FPGAs, Application Note by Ashok Chotai, XAPP 126 June 14 1999 (version 1.1) (Application Note file: xapp126.pdf).

- XC18V00 Series of In-System Programmable Configuration PROMs, Product Specification, DS026 (v2.3) July 5, 2000 (Data Sheet file: ds026.pdf).

- Virtex 2.5V Field Programmable Gate Arrays, Final Product Specification, DS003 (v.2.2) May 23, 2000 (Data Sheet file: ds003.pdf).

- Virtex Configuration and ReadBack, Application Note by Carl Carmichael, XAPP 138 March 21, 1999 (Version 1.0) (Application Note file: xapp138.pdf).

Information available on Internet:
http://www.xilinx.com/

[41] Feedback is very welcome.

[42] MIL-STD-1553 is a military standard that defines the electrical and protocol characteristics for a data bus. Information on the 1553 standard is available on the internet from several sources, one of them is: http://www.1553-mil-std.com/

[43] Hex Workshop is a Hex editor software package by BreakPoint Software. Web site: http://www.bpsoft.com/