| LIVESTOCK WATERING | NRCS-NJ DATA SHEET |
| --- | --- |
| Landowner: |  | Date: |  |
| County: |  | Twp: |  | Completed By: |  |

INDICATE NUMBER OF HEAD IN EACH ANIMAL GROUP:

|  | LIVESTOCK DAILY WATER REQUIREMENTS – Gallons per head per day |
| --- | --- |
| No. Head | Species | Penned | Pastured | NRCS Std 614 |
|  | Dairy Cow – Lactating | 20-35 | 25 | 25 |
|  | Dairy Heifer or Yearlings | 6-15 | 10 | N/A |
|  | Beef Cattle | 6-15 | 10 | 12 |
|  | Cow/Calf Pair | 12-20 | 15 | N/A |
|  | Swine | N/A | N/A | 4 |
|  | Horse | N/A | N/A | 12 |
|  | Sheep / Goats / Llama | 1-3 | 2 | 2 |

| TOTAL DAILY WATER REQUIREMENT |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Species |  |  |  |  |  |  |  |  |
| Number of Head |  | ea |  | ea |  | ea |  | ea |
| Gallons/Head/Day |  |  |  |  |  |  |  |  |
| Gallons/Day Total |  | gpd |  | gpd |  | gpd |  | gpd |

| BASIC SYSTEM INFORMATION |  |  |
| --- | --- | --- |
| Will waterers be permanent (winter use) or seasonal? | ( Permanent | ( Seasonal |
| If seasonal, will water supply lines be buried or above ground? | ( Buried | ( Above Ground |
| To highest waterer? | Distance |  | Elevation |  |
| To farthest waterer? | Distance |  | Elevation |  |
| Operator interested in alternative watering methods? | ( Solar Pump | ( Ram Pump |
|  | ( Nose Pump | ( Wind Power |

WATER SOURCE INFORMATION

Groundwater resources are usually more reliable than surface water, but require power for pumping.  Consider condition of existing well water system and impact on other water needs.  Surface water sources tend to be less expensive but may have water quality concerns or unreliable flow.

| ( | Existing Well |  |
| --- | --- | --- |
|  | Well Location |  |
|  | Well or Pump Elevation |  |
|  | Pump Information |  | Make |  | Model |
|  | Pump Information |  | gpm |  | psi |
|  | Pressure Tank Present? | ( | Yes | ( | No |
|  | Pressure Tank Location: |  |
|  | Pressure Tank |  | gallons |  | psi |
|  | Existing Supply Line |  | Diameter |  | Type Pipe |
|  | Hydrant closest to waterer |  | gpm |  | Pipe Size |
| ( | Proposed Well |  |
|  | Well Location |  |
|  | Well Elevation |  |
|  | Pressure Tank Proposed? | ( | Yes | ( | No |
| ( | Stream or Pond (circle one) |  |
|  | Stream or Pond Elevation |  |
|  | Perennial Flow | ( | Yes | ( | No |
|  | Stream Crossing Needed? | ( | Yes | ( | No |
| ( | Spring Development |  |
|  | Perennial Flow | ( | Yes | ( | No |
|  | Spring Information |  | Elevation |  | Flow Rate |

| Common Conversions |
| --- |
| 1 psi | = | 2.31 feet |
| 1 cfs | = | 450 gpm |
| 1 cubic foot | = | 7.48 gallons |
| 1 cubic foot | = | 62.4 pounds |
| 1 gallon | = | 8.34 pounds |

Determine number of watering spaces required:

|  | WATERING SPACES REQUIRED PER PADDOCK |
| --- | --- |
|  | Herd Watering Pattern | Distance from farthest point in paddock to Watering Facility | Percent of Herd at Waterer |
|  | Case I: Individual Watering | Less than 900 feet | 5 % |
|  | Case II: Group Watering | 900 feet or more | 10% |
|  | Sheep | N/A | 100% |

| Paddock or Field Number |  |  |  |  |
| --- | --- | --- | --- | --- |
| Maximum Distance, feet |  |  |  |  |
| Watering Pattern | ( Case I Individ ( Case II Group | ( Case I Individ ( Case II Group | ( Case I Individ ( Case II Group | ( Case I Individ ( Case II Group |

CASE I:

Individual Watering:  Water is available within 900 feet and livestock drink individually:

|  | Spaces | = |  | x | 0.05 | = |  | spaces | Round to: |  | spaces |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Total number of head) |  |  |  |  |  |  |  |  |

CASE II:

Group Watering:  Distance to water is 900 feet or greater and herd drinks as group:

|  | Spaces | = |  | x | 0.10 | = |  | spaces | Round to: |  | spaces |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Total number of head) |  |  |  |  |  |  |  |  |

watering spaces per tank:

Round tanks:  (Need 20 inches of the perimeter per space)

New round tank:  Minimum diameter if animals have access to entire perimeter:

|  | Diameter | = | spaces | x | 0.53 | = |  | ft diameter | Use: |  | ft. diam min. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Watering Spaces) |  |  |  |  |  |  |  |  |

Existing round tank:  Maximum number of watering spaces per tank:

|  | Spaces | = | feet | x | 1.88 | = |  | spaces | Need: |  | tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Diameter of tank in ft) |  |  |  |  | per tank |  |  |  |

rectangular:  (Need 30 inches of perimeter per space)

Existing rectangular tank:  Maximum number of watering spaces per tank:

|  | Spaces | = | feet | x | feet | x | 0.4 | = |  | spaces | Need: |  | tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Length of tank) |  | (Width of tank) |  |  |  |  | per tank |  |  |  |

WATERER TANK CAPACITY RECOMMENDATIONS:

|  | TANK CAPACITY OF WATERER BASED ON REFILL RATE |
| --- | --- |
|  | Trial | Refill Rate | Tank Capacity (gallons) |
|  | 1 | Instantaneous (2 gpm/space) | Tank capacity can be nominal. Nose pump is feasible. |
|  | 2 | 1 hour | 2 gallons/animal |
|  | 3 | 4 hours | 25% of total daily water requirement |
|  | 4 or Sheep | Greater than 4 hours | 100% of total daily water requirement |
|  | 5 | Solar or Unreliable source | 200% of total daily water requirement |

Trial 1:  Tank capacity is not an issue if flow rate is considered instantaneous:

|  | Flow Rate | = |  | x | 2 gpm | = |  | gpm | OK? | ( Yes ( No |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Number of spaces) |  | space |  |  |  |  |  |

Trial 2:  Need minimum tank capacity of 2 gallons per animal if tank can be refilled in one hour:

|  | Tank Size | = |  | x | 2 gallons | = |  | gallons |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Number of animals) |  |  |  |  |  |

Must meet the following minimum refill rate:

|  | Flow Rate | = | Volume of Tank | = | gal | = |  | gpm | OK? | ( Yes ( No |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 60 mins |  | 60 |  |  |  |  |  |

Trial 3:  Need tank capacity of 25% of daily requirement if refill rate is 4 hours:

|  | Tank Size | = |  | x | 0.25 | = |  | gallons |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Daily Water Requirement) |  |  |  |  |  |

Must meet the following minimum refill rate:

|  | Flow Rate | = | Volume of tank | = | gal | = |  | gpm | OK? | ( Yes ( No |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 240 mins |  | 240 |  |  |  |  |  |

Trial 4:  Need tank capacity of 100% of daily requirement if refill rate is more than 4 hours:

|  | Tank Size | = |  | x | 1.00 | = |  | gallons |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Daily Water Requirement) |  |  |  |  |  |

Must meet the following minimum refill rate:

|  | Flow Rate | = | Volume of tank | = | gal | = |  | gpm | OK? | ( Yes ( No |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 1440 minutes |  | 1440 |  |  |  |  |  |

Trail 5:  Need tank capacity of 2 days for solar pump systems or unreliable water supply:

|  | Tank Size | = |  | x | 2.00 | = |  | gallons |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (Daily Water Requirement) |  |  |  |  |  |

Must meet the following minimum refill rate:

|  | Flow Rate | = | Volume of tank | = | gal | = |  | gpm | OK? | ( Yes ( No |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 1440 minutes |  | 1440 |  |  |  |  |  |

# Footnotes

Use NRCS Std 614 values from table above.  Use other references if not listed for animals to be watered.

Multiply (Number of Head) times (Gallons/Head/Day) for (Total Gallons/Day) for that group.

Ram Pump needs stream site with three feet of fall above the pump and at least 1 gpm flow rate during summer.

Nose Pump maximum distance = 300 feet on flat terrain or 125 feet with a 25 foot elevation difference

Animals drink individually when far corner of paddock to the waterer is less than 900 feet.  When water is 900 feet or more away, grazed animals tend to drink as a herd and more watering spaces are required.