WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11137 | In-Flight Anomaly Number -- | Contractor Report Number E-108 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title IMPROPER INSTALLATION OF BOND JUMPERS |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT 3 | Sys_Lvl Y | Misc Codes A (3) B (X) C D E F (X) G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ET COMPLETE | PART# 80901010000 | SER/LOT# LWT-41 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE ELECT. BOND JUMPER | PART# 80901010000 | SER/LOT# N/A | MANUFACTURER MMC |
| Test/Operation M - MFG | Prevailing Condtion N - INSPECTION | F / U F | Fail Mode EV - NOT-TO-SPEC | Cause MAP - MFG-ASY-INST |
| System ELECTRICAL | Defect CN - CONTAM | Material E - EL C/W | Work Contact J. ADAMS | Fail Date 11/17/1987 |
| Received at MSFC 12/31/1987 | Date Isolated -- | FMEA Reference N/A | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EV - NOT-TO-SPEC | Time Cycle N/A |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 05/18/1988 | Defer Date -- | Add Date 01/04/1988 | R/C Codes 5 - TRNG -- -- |
| Assignee |
| Design A. JACKMAN | Chief Engineer A. JACKMAN | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| Approval |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 06/14/1988 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A. A DEFECTIVE BOND JUMPER INSTALLATION WAS FOUND ON THE GOX PRESSURIZATION LINE OF LWT-41 WHILE INVESTIGATING NEARBY DAMAGED HARDWARE. EPOXY PRIMER HAD BEEN LEFT ON THE ALUMINUM STRUCTURE TO WHICH THE BOND JUMPER TERMINAL WAS BOLTED. THE ENGINEERING REQUIREMENTS, STP-6511, REQUIRES BOND JUMPERS TO BE INSTALLED ON EITHER CLEANED AND ABRADED BARE METAL OR CLEANED AND IRRIDITED ALUMINUM. REVIEW OF THE MANUFACTURING PROCESS PLANS FOUND THAT THE PLANS DID NOT PROPERLY IMPLEMENT THE ENGINEERING REQUIREMENTS FOR SURFACE PREPARATION OF THE METAL B. WHILE INVESTIGATING THE PROBLEMS WITH SURFACE PREPARATION FOR BONDING, DESCRIBED IN "A" ABOVE, IT WAS FOUND THAT THE BOND RESISTANCE TESTING, PERFORMED ON EACH COMPLETED BOND, WAS QUESTIONALBLE. THE TEST EQUIPMENT AND TEST METHODS USED COULD RESULT IN A DEFECTIVE INSTALLATION WITH HIGH RESISTANCE INDICATING AN ACCEPTABLY LOW RESISTANCE ON THE OHMMETER REF: ORIGINAL FAILURE - MARS T-98971 AND DR 150365 |
| Contractor Investigation/Resolution R/A - 1) FLEET: MARS ARE WRITTEN FOR ALL DEFECTIVE OR SUSPECT BONDING INSTALLATIONS ON ALL ETS. THE MARS WILL BE BASED ON REVIEW OF THE MPP FOR EACH LOCATION 2) PRODUCTION: REVISED MPP AND TRAINED PERSONNEL CAUSE - A. THE MANUFACTURING PROCESS PLAN WHICH CONTROLLED THE INSTALLATION OF THE JUMPER WERE INCORRECT B. THE PRODUCTION WORKERS AND QUALITY INSPECTORS WERE NOT PROVIDED WITH THE NECESSARY INFORMATION OR EXPERIENCE TO UNDERSTAND AND PERFORM THE BOND RESISTANCE TEST REQUIRED BY STP 6511 AND THE TEST EQUIPMENT HAD UNFORESEEN OPERATING CHARACTERISTICS GENERAL ELECTRICAL BOND JUMPERS AND INHERENT BONDING ARE USED ON THE ET BETWEEN VARIOUS ELECTRICAL AND STRUCTURAL COMPONENTS FOR REASONS OF LIGHTNING PROTECTION, ELECTROMAGNETIC INTERFERENCE PROTECTION, AND STATIC DISCHARGE. THE ENGINEERING REQUIREMENTS FOR SUCH BOND JUMPERS, STANDARD PROCESS 6511, SPECIFIES HOW VARIOUS METALS AND SURFACE COATINGS ARE TO BE PREPARED FOR THE BONDING AS WELL AS SPECIFYING THE MAXIMUM ALLOWABLE RESISTANCE VALUE BETWEEN THE COMPONENTS BEING BONDED A. THE INTENT OF STP 6511 IS THAT ALL UNPLATED METAL SURFACES BE ABRADED PRIOR TO BONDING, WITH THE EXCEPTION OF IRRIDITED ALUMINUM SURFACES. ERRORS IN THE MANUFACTURING PROCESS PLANS INCLUDED DIRECTING THE BOND JUMPERS TO BE INSTALLED OVER: EPOXY PRIMER COVERED ALUMINUM; ZINC CHROMATE LACQUER PRIMED ALUMINUM; ALUMINUM WITH NO SURFACE COATING OF ANY KIND; AND UNABRADED STAINLESS STEEL SURFACES B. COMPLETED BONDS ARE REQUIRED BY STP 6511 TO BE TESTED FOR RESISTANCE ACROSS THE BOND. BOND CLASSES "L" (LIGHTNING PROTECTION) AND "R" (ELECTROMAGNETIC ENERGY GROUNDING) REQUIRE A RESISTANCE OF LESS THAN 2.5 MILLIOHMS. DURING THE REWORK OF IMPROPERLY INSTALLED BOND JUMPERS ON AN ET, SEE "A" ABOVE, AN ENGINEER OBSERVED THAT A HEWLETT PACKARD MODEL 4328A MILLI- OHMMETER GAVE AN ERRONEOUS READING. AN INVESTIGATION INTO THE METER OPERATION FOUND THAT THE HP 4328A IS CAPABLE OF GIVING A MIDSCALE INDICATION ON ITS METER WHEN ONE OF THE "SENSE" LEADS IS NOT IN CONTACT WITH THE PART UNDER TEST. THE OPERATING MANUAL FOR THE HP 4328A MAKES NO MENTION OF THIS CONDITION. THE RESULT OF THIS METER CHARACTERISTIC IS THAT BONDS WITH AN UNACCEPTABLE HIGH RESISTANCE COULD "PASS" WHEN TESTED WITH THE HP 4328A AND OTHER MILLIOHMETERS AND OBTAINED ERRONEOUS READINGS OF "0" MILLIOHMS ACROSS BONDS. (REFERENCE: INTEROFFICE MEMO 3741-88-021) 02/29/88 UPDATE - UPGRADED CRITICALITY TO 1 DUE TO TPS DEBRIS HAZARD BOND JUMPERS HAVE BEEN INSTALLED OVER PAINTED STRUCTURE, FORWARD OF STATION 2058, AND IN THE DIRECT LIGHTING PATH. IN THE EVENT OF A LIGHTNING STRIKE THE JUMPERS WOULD ARC/BURN. TPS OVER THE JUMPERS COULD BE EXPELLED AND MAY STRIKE THE ORBITER 5/19/88 UPDATE: CRITICALITY - THE ELECTRICAL BOND JUMPERS AND STRUCTURAL INHERENT BOND ARE LISTED IN NEITHER THE FMEA NOR THE CIL EVALUATION OF THE ET DESIGN AND SIMULATED LIGHTNING STRIKE TESTS OF THE THRUST STRUT TO LONGERON BOND JUMPER, ENGINEERING TEST REPORT 826-2383, FOUND THAT AN INFLIGHT LIGHTNING STRIKE WOULD EXPEL NO DEBRIS THAT WOULD IMPACT ON THE ORBITER TASK I. FAILURE INVESTIGATION A. MANUFACTURING ENGINEERING, DEPARTMENT 3614, QUALITY ENGINEERING, DEPARTMENT 3743, AND RELIABILITY ASSURANCE, DEPARTMENT 3741, REVIEWED THE MANUFACTURING PROCESS PLANS FOR ALL WORK ASSEMBLED AND TESTED PRIOR TO THE CORRECTIVE ACTIONS LISTED IN TASKS IIA, IIB, IIC, AND IIE. ALL MPPS HAD BEEN CORRECTED BY LWT-49. THE RESULTS OF THE MPP REVIEW WERE USED BY RELIABILITY ASSURANCE TO GENERATE MARS FOR ALL DEFECTIVE INSTALLATIONS (SEE TASK III) B. TEST OPERATIONS, DEPARTMENT 3613, EVALUATED THE VARIOUS BRANDS AND MODELS OF MILLIOHMMETERS CURRENTLY AVAILABLE IN ORDER TO FIND ONE THAT IS BETTER SUITED TO USE ON THE ET THAN THE HP 4328A WHICH IS NOW IN USE. IT WAS DETERMINED THAT THE KEITHLEY MODEL 580 COULD PROVIDE SIMPLER, MORE RELIABLE OPERATION (REFERENCE: INTEROFFICE MEMO 3613-88-059). CONCURRENTLY WITH THE EVALUATION OF NEW METERS, ACTIONS WERE TAKEN TO CONTROL THE USE OF THE HP 4328A SO AS TO PROVIDE ASSURANCE THAT MEASUREMENTS ARE MADE CORRECTLY (SEE TASKS IIA, IIB, AND IIC) NOTE: KEITHLEY MODEL 580 METERS ARE ON ORDER AND WILL REPLACE THE HP 4328A METERS WHEN THEY ARE AVAILABLE AND THE WORKERS HAVE BEEN TRAINED IN THEIR USE (REFERENCE: PURCHASE ORDER NO. R53418) TASK CLOSED TASK II CORRECTIVE ACTION A. ELECTRICAL ENGINEERING, DEPARTMENT 3514, AND MISSION SUPPORT, DEPARTMENT 3545, REVISED THE TESTING REQUIREMENTS FOR BONDS CHANGE SUMMARY B01815-001, RCN 108 (PRCN L-ED) ADDED THE REQUIREMENT TO USE TEST PROCEDURE TP-7J01-FT TO THE "ET FLIGHT ACCEPTANCE REQUIREMENTS, MMC-ET-TM04K-B, PARAGRAPH 2.2.6.2" B. TEST OPERATIONS ENGINEERING, DEPARTMENT 3613, AND QUALITY ENGINEER- ING, DEPARTMENT 3743, ISSUED TEST PROCEDURE TP-7J01-FT, PCN45, APPENDIX 9.3.30, TO CONTROL BONDING RESISTANCE MEASUREMENTS THE NEW TEST PROVIDES SUFFICIENT CONTROLS TO PREVENT DEFECTIVE BONDS PASSING THE RESISTANCE TEST DUE TO TEST EQUIPMENT CHARACTERISTICS OR TEST METHOD ERRORS. THE TEST PROCEDURES REQUIRES THAT THE WORKERS HAVE THE CERTIFICATION FOR MILLOHMMETERS ITEM CLOSED C. TRAINING, DEPARTMENT 3084, AND ADVANCED MANUFACTURING TECHNOLOGY, DEPARTMENT 3693, DEVELOPED A CERTIFICATION COURSE FOR THE USE OF MILLIOHMMETERS WHICH INCLUDES COVERAGE OF THE REQUIREMENTS OF TEST PROCEDURE TP-7J01-FT. ALL WORKERS WHO PERFORM BONDING RESISTANCE MEASUREMENTS HAVE BEEN TRAINED ITEM CLOSED D. "GOVERNMENT-INDUSTRY DATA EXCHANGE PROGRAM (GIDEP) ALERT" NUMBER MMC-ET-RA07B-29 HAS BEEN SUBMITTED TO THE MSFC ALERT COORDINATOR TO INFORM INDUSTRY OF THE UNIQUE OPERATING CHARACTERISTICS OF THE HEWLETT PACKARD MODEL 4328A MILLIOHMMETER ITEM CLOSED E. ADVANCED MANUFACTURING TECHNOLOGY, DEPARTMENT 3693, AND MANUFACTURING ENGINEERING, DEPARTMENT 3614, RETRAINED THE PERSONNEL RESPONSIBLE FOR WRITING THE MPPS IN THE PROPER METHODS OF SURFACE PREPARATION FOR BONDING PER PI-6511 (REFERENCE: INTEROFFICE MEMO 3693-87-RM-131) ITEM CLOSED NOTE: CHANGE SUMMARY B01831, WHICH IS THE PROCESS OF REVISION AND AND APPROVAL, WILL IMPROVE THE CLARITY OF STP-6511 AS WELL AS MAKING IMPROVEMENTS IN THE BONDING METHODS. AS A RESULT OF THE STP CHANGE, THE PI WILL SUBSEQUENTLY BE REVISED F. MANUFACTURING ENGINEERING, DEPARTMENT 3614, AND QUALITY ENGINEERING, DEPARTMEMT 3743, CORRECTED THE MPP STEPS FOR THE INSTALLATION AND TESTING OF ELECTRICAL BONDS. THE MPPS THAT HAD NOT YET BEEN USED TO ASSEMBLE HARDWARE WERE CORRECTED BEGINNING WITH LWT-42 ALL MPPS FOR LWT-49 AND SUBSEQUENT HAVE BEEN CORRECTED. (REFERENCE: INTEROFFICE MEMOS 3614-88-116 AND 3614-88-040) ITEM CLOSED TASK III CLEARANCE OF EFFECTIVITIES MARS WERE WRITTEN FOR ALL DEFECTIVE OR SUSPECT BONDING INSTALLATIONS ON ALL ETS. THE MARS WERE BASED ON A REVIEW OF THE MANUFACTURING PROCESS PLANS FOR EACH LOCATION (SEE TASK IA). A COMPLETE LIST OF THE MARS IS PROVIDED AS ATTACHMENT 1 TO THIS CAPS TASK CLOSED TASK IV. CLOSURE SUMMARY THE MANUFACTURING PROCESS PLANS FOR THE INSTALLATION OF ELECTRICAL BOND JUMPERS CONTAINED ERRORS THAT AFFECTED THE ELECTRICAL PERFORMANCE OF THE BONDS. THE TEST METHODS USED TO MEASURE THE RESISTANCE OF THE BONDS COULD PASS DEFECTIVE HARDWARE THE PERSONNEL THAT WRITE THE MPPS WRE RETRAINED. THE TEST METHODS FOR BOND RESISTANCE CHECKS WERE CHANGED AND INCLUDED IN A FORMAL TEST PROCEDURE. THE WORKERS THAT PERFORM THE RESISTANCE TESTS HAVE BEEN TRAINED AND CERTIFIED. ALL NONCONFORMING AND SUSPECT HARDWARE HAS BEEN DOCUMENTED ON MARS TASK CLOSED THIS CLOSURE IS SUBMITTED TO MSFC FOR REVIEW AND APPROVAL LISTED BELOW, BY EFFECTIVITY, ARE ALL OF THE MARS THAT WERE WRITTEN FOR DEFECTIVE BOND JUMPER INSTALLATIONS AND FOR IMPROPERLY PERFORMED BOND RESISTANCE TESTS LWT-16 T-96020, T-96021, T-96023, T-97502, T-99764 LWT-20 T-100144, T-100145, T-100146, T-100147 LWT-21 T-96016, T-96017, T-96024, T-97503 LWT-22 T-100156, T-100157, T-100161, T-100162 LWT-24 T-100164, T-100165, T-100166, T-100167 LWT-25 T-100135, T-100137, T-100138, T-100139 LWT-26 T-100140, T-100141, T-100142, T-100143 LWT-27 T-100131, T-100132, T-100133, T-100134 LWT-28 T-100127, T-100128, T-100129, T-100130 LWT-29 T-100123, T-100124, T-100125, T-100126 LWT-30 T-100105, T-100106, T-100107, T-100109 LWT-31 T-100155, T-100152, T-100153, T-100154 LWT-32 T-100185, T-100186, T-100172, T-100173 LWT-33 T-100179, T-100182, T-100183, T-100184 LWT-34 T-100110, T-100112, T-100113, T-100114 LWT-35 T-100192, T-100193, T-100194, T-100195 LWT-36 T-100119, T-100120, T-100121, T-100122 LWT-37 T-100190, T-100115, T-100116, T-100117, T-100118 LWT-38 T-100191, T-100180, T-100101, T-100103, T-100104 LWT-39 T-100197, T-100174, T-100175, T-100176, T-100199 LWT-40 T-96018, T-96019, T-96022, T-96025, T-98046 LWT-41 T-94029, T-94030, T-97265, T-99765 LWT-42 T-98042, T-98044 LWT-43 T-99762, T-99763 LWT-44 THROUGH 48 (COMPONENTS) T-78026, T-78042, T-78039, T-78027, T-78044, T-78041, T-78033, T-78040, T-78035, T-78036, T-78028, T-78038 |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11137 | IFA# -- | Contractor RPT# E-108 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80901010000 | Asmnt Part Name ELECT. BOND JUMPER | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD 3 | CAUSE CD MAP - MFG-ASY-INST | FAIL MODE EV - NOT-TO-SPEC |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |