MEMORANDUM

SUBJECT:	Summary of Environmental and Cost Impacts of Proposed Revisions to Portland Cement New Source Performance Standards (40 CFR Part 60, subpart F)

FROM:	Mark Bahner, RTI

Melissa Icenhour, RTI

Mike Laney, RTI

Keith Barnett, EPA

TO:	Docket Number EPA-HQ-OAR-2007-0877

DATE:	May 29, 2008

I. Introduction

To meet the requirements of section 111(b)(1)(B) of the CAA, the Environmental Protection Agency (EPA) is currently conducting the fourth review of the new source performance standards (NSPS) for Portland Cement Plants (PCP). The PCP NSPS was promulgated on December 23, 1971 (40 CFR Part 60 subpart F, 36 FR 24876) and subsequently reviewed three times (39 FR 20793, June 14, 1974; 39 FR 39874, November 12, 1974; and 53 FR 50354, December 14, 1988). Subpart F requires new, modified, or reconstructed affected facilities at PCP to achieve emission levels that reflect the best demonstrated system of continuous emission reduction, considering cost, non-air quality health, environmental, and energy impacts. These emission levels, referred to as “best demonstrated technology (BDT),” are specified in subpart F.

The purpose of this memorandum is to document the methodology used to estimate the environmental and cost impacts associated with this NSPS review. The impacts in this memorandum are based on a projected number of 20 new kilns over the five year period following promulgation. Section II discusses the impacts of this NSPS review (scheduled for promulgation in 2009), including an overview of the proposed amendments resulting in impacts and the methodology used to develop the impact estimates.

II. Subpart F Impacts Estimated for 2009 Promulgation of NSPS Review

- Affected Industry and Proposed Changes to Subpart F

The portland cement manufacturing industry is comprised of an estimated 105 cement plants capable of producing clinker and operating a total of approximately 178 kilns (PCA, 2007). Based on industry capacity expansion estimates (PCA, 2006), it is projected that by the fifth year following promulgation of the amendments, 20 new kilns will come on line and clinker production capacity will increase by approximately 24,000,000 tons.

To illustrate impacts of the proposed NSPS for cement manufacturing, impacts are calculated for a preheater/precalciner kiln having a clinker production capacity of 1,200,000 tons per year, which is considered representative of new preheater/precalciner kilns. Because of their energy efficiency and higher production capacity, all new kilns are expected to be preheater/precalciner kilns. Impacts are also estimated for the fifth year after promulgation, in which it is assumed that 20 new kilns, each producing 1,200,000 tons of clinker per year will have been built.

The current subpart F NSPS review is scheduled to be promulgated in 2009. The impacts of concern for the NSPS review are incremental impacts, specifically the difference in impacts associated with the current NSPS and the impacts associated with any changes in NSPS requirements resulting from the 2009 NSPS amendments. The impacts are determined over a period of five years following promulgation of the 2009 NSPS revisions. Thus, the affected facilities of concern are those installed from 2009 to 2013. Baseline represents the impacts associated with application of the current NSPS. The incremental impacts of the 2009 NSPS review are determined by comparison to the baseline impacts. Changes in requirements being proposed as part of the 2009 NSPS review that could result in significant incremental impacts include those summarized in Table 1.

Table 1. Summary of proposed changes to subpart F and type of incremental impacts.

| Proposed rule change | Type of Incremental Impact |
| --- | --- |
| ▪ A reduction in the PM stack emission limit for kilns from 0.5 lb of PM/ton of clinker (0.3 lb/ton of feed) to 0.086 lb of PM/ton of clinker. | Costs to replace standard fabric bags with more expensive membrane bags. Emission reductions are also estimated. |
| ▪ A reduction in the PM stack emission limit for clinker coolers from 0.17 lb of PM/ton of clinker (0.1 lb/ton of feed) to 0.086 lb of PM/ton of clinker. | Clinker coolers are already meeting the new limit, but the cost of bag leak detectors are estimated. |
| ▪ Addition of a NOx limit of 1.5 lb NOx /ton clinker. | Costs to install SNCR. Emission reductions are also estimated. |
| ▪ Addition of a SO2 limit of 1.33 lb SO2/ton clinker or 90% reduction of SO2 across the control device. | Costs to install alkaline wet scrubbers. Emission reductions are also estimated. |
| ▪ Addition of bag leak detectors on all new baghouses. | Capital costs of installation and annual costs of operation. |
| ▪ Addition of continuous NOx monitors on new kilns. | Capital costs of installation and annual costs of operation. |
| ▪ Addition of continuous SO2 monitors on new kilns. | Capital costs of installation and annual costs of operation. |
| ▪ Addition of continuous flow monitors on new kilns. | Capital costs of installation and annual costs of operation. |

The air quality impacts and costs of the final amendments for portland cement manufacturing were calculated using the following assumptions:

- Wet alkaline scrubbers will be installed on four new kilns for the control of SO2 emissions;

- New kilns will be equipped with reverse air baghouses using membrane bags rather than fabric bags;

- SNCR will be installed on all new kilns to control NOx emissions;

- NOx monitors will be installed on all new kilns;

- SO2 monitors will be installed on all new kilns; and

- Bag leak detectors will be installed on baghouses on all new kilns and clinker coolers.

- Air Quality Impacts

The various impacts on emissions of nitrogen oxides (NOx), sulfur dioxide (SO2) and particulate matter (PM) are calculated for different control options. These control options will be summarized in the discussion of air quality impacts, below. Direct air impact reductions will be calculated, and where appropriate, indirect air impacts will be calculated, such as the increase in emissions from additional electricity or fossil fuel require to power control devices, water quality impacts (e.g., from scrubbers), and solid waste impacts (e.g., from disposal of spent sorbents or catalysts).

Nitrogen Oxides (NOx)

EPA recently issued an alternative control techniques (ACT) document addressing the emissions and control of NOx from new cement kilns (EPA, 2007). Unless noted otherwise, this document is the source of the information on NOx emissions and controls presented here.

The high temperatures and oxidizing atmospheres required for cement manufacturing are favorable for NOx formation. In cement kilns, NOx emissions are formed during fuel combustion primarily by the oxidation of molecular nitrogen present in combustion air (referred to as thermal NOx) and the oxidation of nitrogen compounds in fuel (referred to as fuel NOx). Many states issuing construction and operating permits for new kilns have specified emission limits for NOx. In recently built kilns, emissions of NOx are typically reduced through process controls such as burner design and staged combustion in the calciner (SCC). NOx emissions from kilns using process designs such as low NOx burners and SCC average about 2.5 lb/ton of clinker (EPA, 2007). Add-on controls used to reduce NOx emissions include selective noncatalytic reduction (SNCR) and selective catalytic reduction (SCR). In recent new source review procedures, states have determined best available control technology (BACT) to be SNCR in addition to well designed SCC and other process designs such as low NOx burners. In SNCR systems, ammonia, urea or another reagent is injected in the flue-gas into an appropriate temperature zone and at an appropriate ratio of ammonia to NOx. On average, SNCR achieves approximately a 35 percent reduction in NOx at a ratio of ammonia-to-NOx of about 0.5 and a reduction of 63 percent at an ammonia-to-NOx ratio of 1.0. At high ratios, some ammonia may not react with NOx and will be emitted (ammonia slip). Another NOx control technology, SCR, is used in the electric utility industry to reduce NOx emissions from boilers and, to date has been used worldwide on three cement kilns. SCR is capable of reducing NOx emission by about 80 percent. Currently, SCR is not used on any cement kilns in the U.S.

Four options were evaluated for control of NOx emissions. The first option was to maintain the baseline of no limit and no additional control. The other three options are given in terms of pounds of NOx per ton of clinker (lb/ton clinker). The three options evaluated were 1.95 lb/ton clinker, 1.5 lb/ton clinker, and 0.5 lb/ton clinker.

In choosing these NOx emission limit options, recently issued permits, recent BACT determinations and recent emissions data for preheater/precalciner kilns were reviewed. At three recently permitted preheater/precalciner kilns utilizing well designed and operated process designs including SCC, averaged NOx emissions of 1.62, 1.88 and 1.97 lb/ton of clinker were measured for Titan America-Pennsuco, in Medley, FL, Little Giant Cement in Harleyville, SC, and CEMEX in Santa Cruz, CA (Bahner, 2008a). These kilns are not equipped with additional add-on controls. However, based on data from equipment vendors and other facilities with more difficult to burn raw materials, we believe that future well-designed and operated cement kilns, which will incorporate SCC and low-NOx burners, will meet a level of 2.5 lb/ton of clinker on average. This level is the baseline level of control that would occur with no additional regulatory action.

The second control evaluated was 1.95 lb/ton clinker, which is a common level established as BACT in recent permits for new sources (Bahner, 2007). As previously noted, some new facilities meet this level of control using low-NOx burners and SCC. However, we expect that, on average, new facilities would require a SNCR removal efficiency of 22 percent SNCR to meet this level, which is well within the range demonstrated for SNCR.

The third control level evaluated was 1.5 lb/ton clinker, and was established based on our assessment of the best demonstrated performance of SNCR. Data on SNCR show a performance that ranges from approximately 20 to 80 percent NOx reduction. We estimate that about 50 percent NOx emission reductions represents a reasonable level of performance of SNCR over the long term. Though new kilns on average will have emissions of 2.5 lb/ton prior to the application of add-on controls, there may be some situations where specific raw materials properties will result in higher NOx emissions. For this reason we assumed a maximum baseline of 3.0 lb/ton and 50 percent emission reduction by SNCR to establish a 1.5 lb/ton control level. Data available for Suwannee American Cement Company, which operates with SNCR, indicated an average NOX value of 1.44 lb/ton, and a calculated 99th percentile 30-day rolling average value of 1.58 lb/ton (Bahner, 2008a).

The fourth option evaluated was 0.5 lb/ton of clinker based on the performance of SCR. There are currently no operating SCR systems on cement kilns in the United States, so SCR currently is not demonstrated in the U.S.

Table 2 shows the NOx annual reductions achieved for each option, for a single kiln producing 1,200,000 tons per year (tpy) of clinker, and nationwide for 20 kilns, each producing 1,200,000 tpy of clinker. Emissions reductions are presented both cumulatively from the baseline and incrementally compared to the next less-stringent measure. For example, for the four emission limit options of 2.5, 1.95, 1.5 and 0.5 lb/ton of clinker, the decreases in lb/ton of clinker relative to the next less stringent option are 0, 0.55, 0.45 and 1 lb/ton, respectively. In contrast the total reductions (relative to the 2.5 lb/ton baseline level) are 0, 0.55, 1, and 2 lb/ton, respectively. Table 2 also presents both the incremental and total emission reductions for a single kiln producing 1.2 million tpy of clinker. As an example of how these reductions are calculated, for a 1.2 million tpy kiln emitting at 1.5 lb/ton (Option 3) versus 2.5 lb/ton (Option 1), the total reduction would be 600 tons (i.e., 2.5 lb/ton minus 1.5 lb/ton, or 1.0 lb/ton, times 1.2 million tpy, or 1.2 million pounds, or 600 tons). Table 2 also has annual nationwide reductions, based on 20 new kilns operating at 1.2 million tpy each over the 5-yr period after promulgation,. Nationwide emission reductions are calculated incrementally (i.e., compared to the next most stringent option) and in total (compared to the baseline, Option 1).

Table 2. Options considered for NOx reductions from kilns.

| Option | Emission Factors, per ton of clinker | Per Kiln Reductions (@1.2 million tpy kiln production) | Annual Nationwide Reductions (based on 20 kilns of 1.2 million tpy each) |
| --- | --- | --- | --- |
|  | Emission Limit (lb/ton) | Incremental Reduction (lb/ton) | Total Reduction (lb/ton) | Incremental Reduction (tons) | Total Reduction (tons) | Incremental (tons) | Total (tons) |
| 1 | 2.5 | 0 | 0 | 0 | 0 | 0 | 0 |
| 2 | 1.95 | 0.55 | 0.55 | 330 | 330 | 6,600 | 6,600 |
| 3 | 1.5 | 0.45 | 1 | 270 | 600 | 5,400 | 12,000 |
| 4 | 0.5 | 1 | 2 | 600 | 1,200 | 12,000 | 24,000 |

Particulate Matter (PM)

All new kilns are expected to use fabric filters for PM control. Fabric filters are the most common PM control technology used for portland cement processes. In selecting the proposed PM emission limit for new kilns, three control options were considered that represented the emissions limits achievable for fabric filters applied to cement kilns. One option was the current level of 0.3 lb/ton of feed (which is equivalent to 0.5 lb/ton of clinker).

The second option was to set a new level that was equivalent to PM levels established as part of recent BACT determinations. These levels range from 0.09 to 0.28 lb/ton of clinker with an average of 0.16 lb/ton of clinker. The second option was chosen as the average value of 0.16 lb/ton of clinker. Current fabric filter designs for new preheater/precalciner kilns routinely achieve this level (Bahner, 2008b).

The third PM control level considered was 0.086 lb/ton clinker. This is the level equivalent to the currently proposed new source level for cement kilns that fire hazardous waste. In order to evaluate control device that are representative of the latest fabric filter design, 19 emission tests conducted on four portland cement kilns controlled by fabric filters with membrane bags, where the kilns had been built in the last 10 years, were reviewed,.  Thirteen of those tests were on a cement kiln that burns hazardous waste.  No difference is expected in the performance of a fabric filter for PM applied to a kilns that burn hazardous waste and those that do not because PM emissions are largely contributed by non-hazardous waste feed streams, and because fabric filters control PM emissions generally to the same concentration irrespective of the PM loading at the inlet.  The individual test results converted to an output basis ranged from 0.0023 to 0.10176 lb/ton of clinker with an average of 0.0357 lb/ton.  In order to account for variability, statistical variation was analyzed by calculating a standard deviation of the test averages, multiplying the standard deviation by the t value for the 95th or 99th percentile, and adding this value to the average of all the tests.  A level of 0.0830 lb/ton of clinker represented an emissions limit that will not be exceeded 95 percent of the time and a level of 0.1025 lb/ton of clinker represented an emissions limit that will not be exceeded 99 percent of the time.  The emission test results and results of the statistical analysis are presented in Attachment 5.

A different statistical analysis of the data from the hazardous waste-burning cement kiln equipped with a membrane fabric filter was performed, applying to the data a so-called universal variability factor derived from the performance of the best performing (lowest emitting) PM performers equipped with fabric filters across the hazardous waste combustor source category.  This variability factor quantifies both short-term and long-term operating variability, i.e., variability associated with the conditions of the individual compliance test and variability associated with the performance of the control equipment over time.  (See 72 FR 54878-79, September 27, 2007.)  (This approach is more sophisticated, since it accounts for both short-term and long-term variability, whereas variability in the individual runs comprising the compliance tests (i.e., the 95th or 99th percentile of those data), is more a measure of short-term variability alone, see 72 FR 54878).  Using this approach, a value of 0.0069 gr/dscf, corrected to 7 percent oxygen, was calculated.  (See 71 FR 14669, March 23, 2006.)  Using a typical value of 54,000 dry standard cubic feet (dscf) of exhaust produced per ton of kiln feed and one ton of clinker producer per 1.65 tons of feed, 0.0069 gr/dscf is equivalent to 0.086 lb/ton of clinker. At this control level, more expensive membrane-coated bags would be needed to replace standard fabric bags in the fabric filter.

Table 3 shows the PM reductions that can be achieved under each option for a single model producing 1,200,000 tons per year (tpy) of clinker, and nationwide for twenty kilns, each producing 1,200,000 tpy of clinker. Emissions reductions are presented both cumulatively from the baseline if possible, and incrementally compared to the next less-stringent measure.

Table 3. Options considered for PM reductions from kilns.

| Option | Emission Factors, per ton of clinker | Per Kiln Emission Reduction (@1.2 million tpy kiln production) | Nationwide Emission Reductions (based on 20 kilns of 1.2 million tpy each) |
| --- | --- | --- | --- |
|  | Emission Limit (lb/ton) | Incremental Reduction (lb/ton) | Total Reduction (lb/ton) | Incremental Reduction (tpy) | Total (tpy) | Incremental (tpy) | Total (tpy) |
| 1 | 0.5 | 0 | 0 | 0 | 0 | 0 | 0 |
| 2 | 0.16 | 0.34 | 0.34 | 204 | 204 | 4,080 | 4,080 |
| 3 | 0.086 | 0.074 | 0.414 | 44.4 | 248.4 | 888 | 4968 |

Sulfur Dioxide (SO2)

Based on reviews of recent BACT determinations and permits, control technologies that were not being used at the time of the previous NSPS review are now being used to control SO2 emissions from cement kilns. As a result, wet scrubbers and lime injection were evaluated as potential control technologies for portland cement operations. The proposed emission limit takes into account the inherent scrubbing ability of the naturally alkaline raw materials used in the cement manufacturing process.

Sulfur dioxide from a cement kiln comes from the oxidation of sulfur from two sources. The first is sulfur in the fuel, which mixes with lime in the kiln and preheater with little or no SO2 emitted into the atmosphere from this source. The other source of SO2 is the raw materials, which may be oxidized to SO2 in the kiln system when mixed with sufficient oxygen.

For most portland cement plants, the levels of sulfur in raw materials are sufficiently low and most of the SO2 generated is removed by the natural scrubbing action of the kiln raw feed. In instances where the sulfur content of raw materials is higher, uncontrolled SO2 emissions can be significant. In those situations, add-on controls may be necessary to prevent high SO2 emissions.

The first type of SO2 control equipment considered is alkaline scrubbers. They are capable of achieving a 90 to 95 percent reduction in SO2 emissions on cement kilns (Bahner and Laney, 2008). The difference between SO2 emissions before and after the scrubber at the Lehigh Cement plant in Davenport, Iowa was approximately 96 percent (Bahner, 2008c; Bahner and Laney, 2008).

The second type of SO2 control equipment is lime injection, which consists of injecting lime into a duct downstream of the preheater, or in some cases injecting lime into the first two preheater stages to remove SO2. At some facilities lime injection is only used when increases on SO2 emission above a specified level are detected, such as when the raw mill is down. Dry lime systems typically achieve an emission reduction of approximately 70 percent (NESCAUM, 2005), although there are systems that can achieve 90 percent. (Bahner and Laney, 2008).

Four options were evaluated for control of SO2 emissions. The first option was to maintain the baseline of no SO2 emission limit, and the other three options include an emission limit of SO2 in pounds per ton of clinker (lb/ton clinker). Air quality impacts under each of the control options depend on the sulfur content of the raw materials. Raw materials containing high levels of sulfur are likely to result in high SO2 emissions unless controls are applied.

High uncontrolled SO2 emissions associated with high sulfur raw materials were based on examples where facilities have applied wet scrubbers for SO2 control and were assumed to emit uncontrolled SO2 at a level of 13 lb/ton. Uncontrolled SO2 emissions of 1.3 lb/ton of clinker (0.8 lb/ton of feed) represent a moderate emission level. The moderate uncontrolled SO2 emission level was based on the averages of 18 data points for tested NSPS facilities and was assumed to represent moderate raw material sulfur levels (Heath, 1996). Low uncontrolled SO2 emissions from low sulfur raw materials are based on examples from Florida where kilns emit uncontrolled SO2 at levels of 0.2 lb/ton clinker or less (Bahner, 2008c).

The first control option was no additional control of SO2 other than the inherent control achieved by the kiln and raw mill. State BACT determinations usually identify inherent SO2 removal as BACT. The second option selected was 1.33 lb/ton clinker which represents a recent BACT determination level of a facility (TXI, Midlothian, TX) with high sulfur raw materials that applied an alkaline wet scrubber for SO2 control (FL DEP, 2005). The third option evaluated was 0.4 lb/ton clinker, which is based on the average of SO2 permit limits from recent BACT determinations which ranged from 0.06 to 1.33 lb/ton of clinker (Bahner, 2007). The fourth option evaluated was 0.2 lb/ton clinker which is typically specified in Florida for kilns with low sulfur raw materials and is one of the lowest levels from recent BACT determinations.

The proposed SO2 emission limit for new kilns is 1.33 lb/ton of clinker, or alternatively, demonstration of a 90 percent SO2 emissions reduction measured across the control device, such as an alkaline scrubber as BDT. Option 1 would have allowed kilns with high sulfur raw materials, several of which are currently controlled with wet scrubbers, to emit significant amounts of SO2.

Table 4 shows the SO2 reductions that can be achieved by a wet scrubber that gets a SO2 emission reduction of 95 percent under option 1 and 2 for high sulfur kiln input materials. The emission reduction is the same under options 3 and 4.

Table 4. Options considered for SO2 reductions for kilns with high-sulfur inputs.

| Option | Emission Limit (lb/ton clinker) | Control | Annual Emissions (@1.2 million tpy kiln production) (tons) | Annual Reductions (tons) |
| --- | --- | --- | --- | --- |
| 1 | Baseline (13) | None | 7,800 | 0 |
| 2 | 1.33 | Wet scrubber | 390 | 7,410 |

Table 5 shows the SO2 reductions that can be achieved by option for medium sulfur kiln input materials. For option 2, no additional control is necessary because the uncontrolled emission level is below the SO2 limit of 1.33 lb/ton. Under option 3, a less costly lime injection system that gets 70 percent removal is capable of meeting the limit of 0.4 lb/ton. A wet scrubber would be required under option 4.

Table 5. Options considered for SO2 reductions for kilns with medium-sulfur inputs.

| Option | Emission Limit (lb/ton clinker) | Control | Annual Emissions (@1.2 million tpy kiln production) (tons) | Reductions (tons) | Emission Level After Control (lb/ton clinker) |
| --- | --- | --- | --- | --- | --- |
| 1 | Baseline (1.3) | None | 780 | 0 | 1.3 |
| 2 | 1.33 | No reduction necessary | 780 | 0 | 1.3 |
| 3 | 0.4 | Dry lime scrubber (DLS) (70%) | 234 | 546 | 0.39 |
| 4 | 0.2 | Wet scrubber (WS) (95%) | 39 | 741 | 0.065 |

For kilns with uncontrolled emissions (due to low sulfur input materials, combined with the natural scrubbing effect of alkali materials in the kiln) below 0.2 lb/ton, no controls for SO2 will be necessary. The baseline SO2 emissions from a kiln producing 1.2 million tons per year would be 120 tpy (i.e., 1.2 million tons per year times 0.2 lb/ton).

It is estimated that, nationwide, four kilns will be using high-sulfur raw materials in the five years following promulgation. The emission reductions in the fifth year will be 7,410 tpy times 4 kilns = 29,640 tpy.

VOC and CO

Emissions of CO and unburned hydrocarbons (VOC/THC) are due to incomplete oxidation. Methods to address these pollutants include more complete oxidation either in the burner area (e.g. with higher levels and better placement of the introduction of excess air) or by more complete oxidation in a downstream control device, such as a regenerative thermal oxidizer (RTO, where the “regenerative” portion of the description refers to recovery of heat that would otherwise be lost in the oxidation process). The VOC/THC from raw materials can be significant if there are substantial organics in the raw material. The only control technology identified to reduce CO emission is an RTO (which also would concurrently reduce any VOC emissions). Activated carbon injection (ACI) into a particulate control device can be used to control VOC/THC (but not CO).

The proposed amendments will not contain limits for CO or VOC emissions from cement kilns. VOC emission from new cement kilns will mainly result from organics in the raw materials. Organic constituents in the raw material can be driven off in the kiln preheater prior to reaching a temperature zone that would result in combustion. New cement kilns are currently subject to a 20 ppmv total hydrocarbon (THC) emissions limit by the Portland Cement NESHAP.  Because most of the THC are also VOC, the THC limit also limits VOC, and serves as the baseline for the NSPS analysis.  This limit is based on the best performance of the regenerative thermal oxidizer add-on control, which is the most effective VOC emission control available for this source category.  Therefore we determined that no additional regulation of VOC emissions is feasible.

Emissions of CO can come from two sources, unburned fuel from the precalciner and CO evolved from the raw materials by the same mechanism as the THC emissions. Unburned fuel represents an economic loss to the facility. Therefore, new precalciners are designed to combust fuel as efficiently as possible, and CO emissions from fuel combustion are minimized, regardless of any potential emission limit.

As is the case for VOC, facilities with moderate or high levels of organic materials in the feed would emit THC at levels high enough that THC control would be required under the Portland Cement NESHAP. Therefore, the THC limit in the Portland Cement NESHAP also serves as the baseline of the CO analysis.  As previously noted, the THC limit is based on the best performance of the regenerative thermal oxidizer add-on control, which is also the most effective CO emission control available for this source category.  Therefore we determined that no additional regulation of CO emissions is feasible.

Secondary Impacts

Secondary air quality impacts will result from the increased electrical demands of control equipment required to comply with the final amendments. The secondary impacts in this memorandum will include impacts of additional electricity consumption and the pollution from that consumption, water pollution, and solid waste impacts. The addition of add-on controls, such as scrubbers, will increase electricity demands. The electricity demand for pumping the reagent in an SNCR system are negligible. The additional electricity usage by an alkaline scrubber for a 1.2 million ton per year plant are as follows (see input parameters for wet scrubber in cost section):

Scrubber	-	12,075,355 kWh/yr

The emission factors used to estimate increased emissions of NOx, CO, SO2, and PM10 from the increased electricity demand are as follows (Docket item IV-B-25, Docket A-94-52):

NOx	-	0.00446 lb/kWhr

CO	-	0.00231 lb/kWhr

SO2	-	0.00765 lb/kWhr

PM10	-	2.25(10-4) lb/kWhr

Increases in secondary emissions resulting from the increased electrical demand of an alkaline scrubber for a new 1,200,000 ton/yr kiln are summarized in Table 6.

Table 6. Secondary emissions for a 1,200,000 tpy kiln.

| Control | Increased Electrical Demand (kWh/yr) | Increased Emissions (tons/yr) for 1.2M Ton/Yr Kiln |
| --- | --- | --- |
|  |  | NOx | CO | SO2 | PM10 |
| Wet Scrubber | 12,075,355 | 26.9 | 13.9 | 46.2 | 1.4 |

The total nationwide increase in emissions from the increased electrical demands of scrubbers installed on four new kilns for the fifth year following promulgation are presented in Table 7.

Table 7. Nationwide secondary emissions.

| Controls and number of systems | Increased Electrical Demand (kWh/yr) | Nationwide Increased Emissions (tons/yr) |
| --- | --- | --- |
|  |  | NOx | CO | SO2 | PM10 |
| Scrubbers (on 4 kilns) | 48,301,420 | 108 | 56 | 185 | 5 |

- Water Quality Impacts

The use of alkaline scrubbers will result in increased consumption of water (for makeup water and production of the scrubber slurry). For a new 1,200,000 ton/yr kiln, the additional water requirement is estimated at 97,000,000 gallons per year (see input parameters for wet scrubber in cost section). No water quality impacts are associated with the use of SNCR systems. Based on the use of scrubbers on a total of four new kilns over the 5-year period following promulgation, total water requirements at the end of the fifth year will be approximately 388 million gallons.

D. Solid Waste Impacts

Additional solid waste will result from the disposal of scrubber slurry. For a new 1,200,000 ton/yr kiln, the additional solid waste generated as a result of the addition of the scrubber is estimated at 84,101 tons per year (Docket item II-B-67, Docket No. A-92-53). However, the waste from the scrubber contains synthetic gypsum and is typically dewatered and returned to the process where it is mixed with clinker in the finish mill. The result is that the waste is not disposed of in a landfill. No solid waste impacts are anticipated with the use of an SNCR system. The total additional solid waste generated at the end of the fifth year following promulgation of the amendments will be an estimated 336,000 tons from the scrubber slurry of four scrubbers.

The additional solid waste generated from baghouses, in the form of cement kiln dust, as a result of the more stringent PM requirement will be 44.4 tons/yr for a 1,200,000 ton/yr kiln. This material is typically considered product and is returned to the kiln or mixed with the cement.

E. Energy Impacts

The use of alkaline scrubbers on new kilns will increase electricity consumption. The additional electricity required for an alkaline scrubber added onto a new 1,200,000 ton/yr kiln is estimated at 12,075,355 kWh/yr.  For the 5-year period following promulgation, the additional electricity demand associated with the installation of scrubbers on four new kilns will be 48,301,420 kWh.

- Cost Impacts

NOx Emissions

Four options were evaluated for control of NOx emissions. The first option was to maintain the baseline of no NOx limits. The other three options are given in terms of pounds of NOx per ton of clinker (lb/ton clinker). The three options evaluated were 1.95 lb/ton clinker, 1.5 lb/ton clinker, and 0.5 lb/ton clinker.

Costs were evaluated for all four options. Costs for SNCR and SCR were derived from Alternative Control Techniques Document Update – NOx Emissions from New Cement Kilns (EPA, 2007). Capital costs for SNCR systems ranged from $0.78 to $2.88 per ton of clinker produced. An average of $1.76 per ton of clinker was used to estimate capital costs. For the 1.95 lb/ton NOx option, an operating cost of $0.51 per ton of clinker was used to calculate annual costs. For the higher removal efficiency necessary to meet the 1.5 lb/ton NOx limit, more reagent would be required to meet the limit resulting in higher operating costs. An average annual cost of $1.01 per ton of clinker was used to estimate annual costs to meet the Option 3 limit of 1.5 lb of NOx /ton of clinker. The average capital costs for SCR were determined to be $4.57 per ton of clinker while an average of $2.50 per ton of clinker was used to estimate annual operating costs for SCR.

The results of this analyses showed that the overall annualized cost of control for both the 1.95 and the 1.5 levels were approximately $2,000 per ton of NOx reduction. Given the similarity of costs, Option 3 (1.5 lb/ton clinker) was chosen as BDT.

Assuming a kiln with a clinker capacity of 1,200,000 tons, the capital cost of the SNCR is $2,112,000 and the annual operating cost is $1,212,000.

Under the proposed amendments, compliance with the emission limits for NOx will be determined using continuous emissions monitoring systems. Continuous flow rate monitors will also be required to determine compliance. The capital/startup costs for NOx and flow rate CEMS are $140,951 and $35,780, respectively. Annual operations and maintenance costs for NOx and flow rate CEMS are $41,809 and $13,864, respectively. All costs are derived from the CEMS Cost Model and include a capital recovery factor of 0.1424 (equipment life of 10 years and a yearly interest rate of 7%). Attachment 2 is the output file from the CEMS Cost Model for NOx CEMS. Attachment 3 is the output file from the CEMS cost Model for flow rate CEMS.

Including the cost of CEMS, the annual operating and maintenance cost per kiln is $1,267,673 and the total capital cost per kiln is $2,288,731 for SNCR. Assuming that 20 new kilns will install SNCR to comply with the NOx emission limit, the total annualized cost is an estimated $25.4 million. Total capital cost over the 5-year period following promulgation is an estimated $45.8 million.

Table 8 shows the costs and potential reductions associated with each of the four options for NOx control.

Table 8. Costs and cost effectiveness of NOx emission limits for 1,200,000 ton/yr kiln.

| Option | 1 (Baseline) | 2 (1.95 lb/ton clinker) | 3 (1.5 lb/ton clinker) | 4 (0.5 lb/ton clinker) |
| --- | --- | --- | --- | --- |
| Capital cost, $million | 0 | 2.3 | 2.3 | 5.7 |
| Annualized cost, $million/yr | 0 | 0.7 | 1.3 | 3.1 |
| Total NOx reduction (tpy) | 0 | 330 | 600 | 1,200 |
| Total C/E ($/ton NOx) | 0 | 2,023 | 2,113 | 2,546 |

Particulate Matter (PM) Emissions

The costs of reverse air baghouses and standard fabric bags (for Options 1 and 2) were derived from the EPA Air Pollution Control Cost Manual. The capital costs of non-membrane bags and a baghouse are estimated to be $4.78 per ton of clinker and annual operating costs are estimated to be $1.67 per ton of clinker. The total costs for a baghouse using standard fabric bags on a kiln with a capacity of 1,200,000 tons of clinker is estimated to be $5,731,163 for capital cost and $2,004,710 for annual cost.

The costs of reverse air baghouses and membrane bags (for Option 3) were also derived from the EPA Air Pollution Control Cost Manual. The capital costs of membrane bags and a reverse air baghouse are estimated to be $5.89 per ton of clinker and annual operating costs are estimated to be $1.82 per ton of clinker. The total cost for a baghouse with membrane bags on a kiln with a capacity of 1,200,000 tons of clinker is estimated to be $7,065,703 for capital cost and $2,180,919 for annual costs.

Because it is assumed that all options would use a reverse air baghouse, the incremental cost of using membrane bags is the difference between the cost of Options 1 and 2 and Option 3. Therefore, the incremental costs are estimated as $1,334,540 for capital cost and $176,209 for annual costs.

Bag leak detectors are used to monitor changes in particulate matter emission rates within baghouses. A change in emission rate usually indicates a bag leak or another type of failure within the baghouse. Costs were estimated using the CEMS Cost Model, assuming that each baghouse has 5 compartments and there is a separate sensor in each compartment. It was assumed that the same bag leak detector could be used for the clinker cooler baghouse as for the kiln baghouse, so the costs were estimated using 10 sensors. The capital/startup cost for bag leak detector CEMS is $93,719. Annual operations and maintenance costs for bag leak detector CEMS are $34,748. All costs are derived from the CEMS Cost Model and include a capital recovery factor of 0.1424 (equipment life of 10 years and a yearly interest rate of 7%). Attachment 4 is the output file from the CEMS Cost Model for bag leak detectors.

Including the cost of the bag leak detector, the annual operating and maintenance cost per kiln is $210,957 and the total capital cost per kiln is $1,428,253 for reverse air baghouses equipped with membrane bags and a bag leak detector for each kiln/clinker cooler combination. Assuming that 20 new kilns and clinker coolers will install reverse air baghouses to comply with the PM emission limit, the total annualized incremental cost is an estimated $4.2 million. Total capital incremental cost over the 5-year period following promulgation is an estimated $28.6 million.

The incremental PM reductions between baseline and Option 3 are estimated to be 44 tons per year. This equals a cost effectiveness of approximately $3,900 per ton of PM reduction. The incremental fine PM reductions (PM less than 2.5 microns in diameter) between baseline and Option 3 are estimated to be 20 tons per year. This equates to a cost effectiveness of approximately $9,000 per ton of fine PM reduction.

SO2 Emissions

Four options were evaluated for control of SO2 emissions. The first option was to maintain the current limit and the other three options include an emission rate of SO2 in pounds per ton of clinker (lb/ton clinker). Control costs and cost reductions for the three emission rates were evaluated based on varying levels of sulfur in the raw materials. Low uncontrolled SO2 emissions from low sulfur raw materials were based on examples from Florida where kilns emit uncontrolled SO2 at levels of 0.2 lb/ton clinker or less. High uncontrolled SO2 emissions associated with high sulfur raw materials were based on examples where facilities had applied wet scrubbers for SO2 control and were assumed to emit uncontrolled SO2 at a level of 13 lb/ton. Uncontrolled SO2 emissions of 1.3 lb/ton represent a moderate emission level. Moderate uncontrolled SO2 emissions were based on the averages of 18 data points for tested NSPS facilities and were assumed to represent moderate raw material sulfur levels.

The first control option considered was no additional control of SO2 other than the inherent control achieved by the kiln and raw mill. State BACT determinations usually identify inherent SO2 removal as BACT. The second option evaluated was an SO2 limit of 1.33 lb/ton clinker which represents a recent BACT determination level of a facility with high sulfur raw materials that applied an alkaline wet scrubber for SO2 control. The third option evaluated was a limit of 0.4 lb/ton clinker, which is based on the average of SO2 permit limits from recent BACT determinations, ranging from 0.06 to 1.33 lb/ton of clinker. The fourth option evaluated was 0.2 lb/ton clinker which is representative of permit limits specified in Florida for kilns with low sulfur raw materials and is one of the lowest levels from recent BACT determinations.

Under the proposed amendments, the SO2 emission limit for new kilns will be 1.33 lb/ton of clinker, or alternatively, demonstration of a 90 percent SO2 emissions reduction measured across the control device, such as an alkaline scrubber as BDT. Option 1 was rejected because this would allow kilns with high sulfur raw materials, several of which are currently controlled with wet scrubbers, to emit significant amounts of SO2. Controlling the high sulfur kilns to a level of 1.33 lb/ton results in a cost per ton of SO2 removed of less than $1000 per ton of SO2 removal.

Options 3 and 4 were rejected because they would have resulted in cement kilns using moderate sulfur content raw materials installing add-on controls at a cost of over $6,000 per ton of SO2 reduction. Also, Options 3 and 4 would not be likely to achieve any significant additional SO2 emission reductions over Option 2 for high sulfur kilns because Option 2 already represents at least a 90 percent emission reduction control for high sulfur raw materials.

Costs for the use of wet alkaline scrubbers on kilns are based on detailed cement industry estimates of retrofitting an existing 804,000 ton per year preheater/precalciner kiln with a wet alkaline scrubber (Zephyr, 2002). The industry cost estimates incorporated costing procedures from the EPA Air Pollution Control Cost Manual. To adapt the industry costs to our new 1,200,000 ton per year kiln, costs were scaled up to account for the difference in exhaust gas flow rates and modified to reflect installation on a new kiln rather than a retrofit. Costs were also updated using Chemical Engineering cost index and a credit applied for the use of the gypsum produced by the scrubber. Scrubbers produce a slurry containing synthetic gypsum, which can be reused in the production of portland cement. A scrubber on a 1.2 million ton/yr kiln is estimated to produce 84,101 ton/yr of gypsum (Docket Item II-B-67, Docket no. A-92-53). Using current estimates from the United States Geological Survey (USGS), the price of gypsum was estimated at $8.26 per ton. Actual costs to purchase gypsum for the production of cement are probably higher primarily due to transportation costs. Assuming that all synthetic gypsum can be reused in the production process, each scrubber has a credit for recycled gypsum of $694,674 per year.

Input parameters and annual cost inputs used in estimating costs are shown in Table 9. Total capital investment for a wet alkaline scrubber installed on a 1,200,000 ton/yr kiln is approximately $28,101,000 and total annual cost, including annualized capital (using 7% interest and a 20-year equipment life), operating costs, and the recycled gypsum credit is approximately $4,913,000. Capital and annual cost for a wet alkaline scrubber on a 1,200,000 ton/yr kiln are shown in Table 10.

Under the proposed amendments, compliance with the emission limits for SO2 will be determined using continuous emissions monitoring systems. Continuous flow rate monitors will also be required to determine compliance. The capital/startup costs for SO2 and flow rate CEMS are $143,135 and $35,780, respectively. Annual operations and maintenance costs for SO2 and flow rate CEMS are $42,326 and $13,864, respectively. All costs are derived from the CEMS Cost Model and include a capital recovery factor of 0.1424 (equipment life of 10 years and a yearly interest rate of 7%). Attachment 1 is the output file from the CEMS Cost Model for SO2 CEMS. Attachment 3 is the output file from the CEMS cost Model for flow rate CEMS.

Including the cost of CEMS, the annual operating and maintenance cost per kiln is $4,969,000 and the total capital cost per kiln is $28,280,000 for alkaline scrubbers. Assuming that four new kilns will install an alkaline scrubber to comply with the SO2 emission limit, the total annualized cost of scrubbers is an estimated $19.9 million. Total capital cost over the 5-year period following promulgation is an estimated $113 million.

The cost of the alkaline wet scrubber is only dependent on the size of the kiln so the costs are identical for any control option that would require the use of alkaline scrubbers, assuming that the scrubber was operated at its highest efficiency.

The amount of SO2 reduction is based on the alkaline scrubber having a removal efficiency of 95% and baseline emissions of 7,800 tons for raw materials with high sulfur content (and high uncontrolled SO2 emissions) and 780 tons for raw materials with moderate sulfur content (and moderate uncontrolled SO2 emissions). It is estimated that alkaline wet scrubbers will result in reductions of 7,410 tpy SO2 for kilns using raw materials with high sulfur content and 741 tpy SO2 for raw materials with moderate sulfur content. The resulting cost effectiveness is approximately $670 per ton of SO2 removed for raw materials with high sulfur content and $6,700 per ton of SO2 removed for raw materials with moderate sulfur content.

Because lime injection may be used to reduce SO2 emissions in certain instances, costs were estimated for a lime injection system for a 1,200,000 ton/yr kiln. Costs are derived from the same source as the wet scrubber costs (Zephyr 2002). Input parameters and annual cost inputs used in estimating costs are shown in Table 11. Total capital investment for lime injection installed on a 1,200,000 ton/yr kiln is approximately $6,997,000 and total annual cost, including annualized capital (using 7% interest) and operating costs is approximately $3,168,000. These costs are shown in Table 12.

Including the cost of CEMS, the annual operating and maintenance cost per kiln is $3,224,000 and the total capital cost per kiln is $7,176,000 for lime injection.

The amount of SO2 reduction is based on lime injection having a removal efficiency of 70% and baseline emissions of 780 tons for raw materials with moderate sulfur content. It is estimated that alkaline wet scrubbers will result in reductions of 540 tpy SO2 for raw materials with moderate sulfur content. The resulting cost effectiveness is $5,970 per ton of SO2 removed for raw materials with moderate sulfur content.

Table 13 shows the costs and potential reductions associated with each of the four options for SO2 control.

Table 9. Wet alkaline scrubber input parameters for new kiln model.

| INPUT PARAMETERS: |  |
| --- | --- |
| -- Clinker production rate, tons/yr | 1,200,000 |
| -- Process operating hours, hr/yr | 7,920 |
| -- Inlet waste gas temperature (oF): | 400 |
| -- Inlet waste gas pressure (atm.): | 1 |
| -- Pollutant in waste gas: | SO2 |
| -- pollutant emissions, lb/yr | 14,475,811 |
| -- pollutant concentration, ppmv | 905 |
| -- pollutant molecular weight | 64 |
| -- Waste gas molecular weight (lb/lb-mole): | 28.85 |
| -- Solvent molecular weight (lb/lb-mole): | 18 |
| -- Inlet waste gas flowrate (acfm): | 330,276.91 |
| -- Scrubber gas pressure drop (in. water): | 17 |
| --Additional system pressure drop (FF and ducts), in. water | 10 |
| -- Liquid pressure drop for pump (ft of H2O): | 60 |
| -- Slurry flow rate, gpm | 19,817 |
| -- Outlet gas temperature, F | 140 |
| -- Makeup water flow, gpm | 105 |
| -- Limestone consumption, tons/hr | 5.4060 |
| -- Estimated control efficiency, percent | 95 |
| -- Electricity consumption, kw |  |
| scrubber and system fans | 1105.0 |
| limestone preparation | 162.2 |
| cooler vent air to stack | 257.4 |
| ANNUAL COST INPUTS: |  |
| Operating factor (hr/yr): | 7,920 |
| Operating labor rate ($/hr): | 22.5 |
| Maintenance labor rate ($/hr): | 24.75 |
| Operating labor factor (hr/sh): | 2.5 |
| Maintenance labor factor (hr/sh): | 2.5 |
| Electricity price ($/kWhr): | 0.062 |
| Limestone, $/ton | 5 |
| Solvent (water) price ($/1000 gal): | 0.2 |
| Overhead rate (fraction): | 0.6 |
| Annual interest rate (fraction): | 0.07 |
| Control system life (years): | 20 |
| Capital recovery factor (system): | 0.0944 |
| Taxes, insurance, admin. factor: | 0.04 |
| Credit for gypsum ($/ton) | 8.26 |
| Gypsum recycled (tons/yr) | 84,101 |

Table 10. Wet alkaline scrubber capital and annual costs for new kiln model.

| CAPITAL COSTS: |
| --- |
| Equipment costs, $ |  |
| -- Limestone handling, milling, and emission control | 1,079,519 |
| -- Scrubber with fans | 5,721,834 |
| -- Scrubber stack | 985,427 |
| -- Bypass, preheater, and cooler vent ductwork; cooler | 1,909,821 |
| vent fan and damper |  |
| -- Sludge handling and material disposal system | 279,734 |
| -- Building and building permit | 1,227,015 |
| -- Contingency (20% of equipment costs) | 2,240,670 |
| -- Total (base) | 7,081,087 |
| Chemical Engineering Plant Cost Index September 2002 | 400.9 |
| Chemical Engineering Plant Cost Index September 2007 | 528.2 |
| ' (escalated) | 9,329,584 |
| Instrumentation (10% of equipment cost) | 932,958 |
| Sales tax (5% of equipment cost) | 466,479 |
| Freight (5% of equipment cost) | 466,479 |
| Purchased Equipment Cost (PEC): | 11,195,501 |
| Direct installation costs, $ |  |
| -- Foundation and supports (12% of PEC) | 1,343,460 |
| -- Handling and erection (60% of PEC) | 6,717,300 |
| -- Electrical (10% of PEC) | 1,119,550 |
| -- Piping (30% of PEC) | 3,358,650 |
| -- Insulation and Ductwork (2% of PEC) | 223,910 |
| -- Painting (2% of PEC) | 223,910 |
| -- Total | 12,986,781 |
| Site preparation cost, $ | 200,000 |
| Indirect installation costs, $ |
| -- Engineering (20% of PEC) | 2,239,100 |
| -- Construction and field expenses (5% of PEC) | 559,775 |
| -- Contractor fees (5% of PEC) | 559,775 |
| -- Start-up (1% of PEC) | 111,955 |
| -- Performance test (1% of PEC) | 111,955 |
| -- Contingencies (3% of PEC) | 335,865 |
| -- Total | 3,918,425 |
| Total Capital Investment ($): | 28,100,706 |

Table 10 (continued)

| ANNUAL COSTS: |  |
| --- | --- |
| Operating labor | 55,688 |
| Supervisory labor | 8,353 |
| Maintenance labor | 61,256 |
| Maintenance materials | 61,256 |
| Replacement parts (5% of PEC) | 559,775 |
| Electricity (fan and pumps) | 669,016 |
| Electricity (limestone preparation) | 79,656 |
| Limestone | 214,079 |
| Solvent (makeup water) | 9,950 |
| Overhead | 111,932 |
| Taxes, insurance, administrative | 1,124,028 |
| Capital recovery | 2,652,508 |
| ------------------------------------------------- |  |
| Total Annual Cost | 5,607,497 |
| Credit for recycled gypsum | 694,674 |
| Total Annual Cost w/ gypsum credit | 4,912,823 |

Table 11. Lime injection input parameters for new kiln model.

| INPUT PARAMETERS: |
| --- |
| -- Clinker production rate, tons/yr | 1,200,000 |
| -- Process operating hours, hr/yr | 7,920 |
| -- Pollutant in waste gas: | SO2 |
| -- pollutant emissions, lb/yr | 14,475,811 |
| -- pollutant molecular weight | 64 |
| -- Solvent molecular weight (lb/lb-mole): | 18 |
| -- Liquid pressure drop for pump (ft of H2O): | 60 |
| -- Makeup water flow, gal/yr | 97,383,410 |
| -- Slurry flow rate, gpm | 4,099 |
| -- Slaked lime consumption, tons/yr | 25,057 |
| -- Estimated control efficiency, percent | 60 |
| -- Electricity consumption, kw | 66.0 |
| ANNUAL COST INPUTS: |
| Operating factor (hr/yr): | 7,920 |
| Operating labor rate ($/hr): | 22.5 |
| Maintenance labor rate ($/hr): | 24.75 |
| Operating labor factor (hr/sh): | 2.5 |
| Maintenance labor factor (hr/sh): | 2 |
| Electricity price ($/kWhr): | 0.062 |
| Slaked lime, $/ton | 65 |
| Solvent (water) price ($/1000 gal): | 0.2 |
| Overhead rate (fraction): | 0.6 |
| Annual interest rate (fraction): | 0.07 |
| Control system life (years): | 15 |
| Capital recovery factor (system): | 0.1098 |
| Taxes, insurance, admin. factor: | 0.04 |

Table 12. Lime injection capital and annual costs for new kiln model.

| CAPITAL COSTS: |
| --- |
| Equipment costs, $ |
| -- Limestone handling system (main and bypass) | 1,271,519 |
| -- Injection system (main and bypass) | 762,911 |
| -- Building permit | 190,728 |
| -- Contingency (20% of equipment costs) | 445,032 |
| -- Total (base) | 2,670,189 |
| Chemical Engineering Plant Cost Index September 2002 | 400.9 |
| Chemical Engineering Plant Cost Index September 2007 | 528.2 |
| ' (escalated) | 3,518,069 |
| Instrumentation (10% of equipment cost) | 351,807 |
| Sales tax (5% of equipment cost) | 175,903 |
| Freight (5% of equipment cost) | 175,903 |
| Purchased Equipment Cost (PEC): | 4,221,683 |
| Direct installation costs, $ |
| -- Foundation and supports (8% of PEC) | 337,735 |
| -- Handling and erection (14% of PEC) | 591,036 |
| -- Electrical (4% of PEC) | 168,867 |
| -- Piping (2% of PEC) | 84,434 |
| -- Insulation and Ductwork (1% of PEC) | 42,217 |
| -- Painting (1% of PEC) | 42,217 |
| -- Total | 1,266,505 |
| Site preparation cost, $ | 200,000 |
| Indirect installation costs, $ |
| -- Engineering (10% of PEC) | 422,168 |
| -- Construction and field expenses (5% of PEC) | 211,084 |
| -- Contractor fees (10% of PEC) | 422,168 |
| -- Start-up (2% of PEC) | 84,434 |
| -- Performance test (1% of PEC) | 42,217 |
| -- Contingencies (3% of PEC) | 126,650 |
| -- Total | 1,308,722 |
| Total Capital Investment ($): | 6,996,909 |
| ANNUAL COSTS: |
| Operating labor | 55,688 |
| Supervisory labor | 8,353 |
| Maintenance labor | 49,005 |
| Maintenance materials | 49,005 |
| Replacement parts (5% of PEC) | 211,084 |
| Electricity (pumps) | 1,622 |
| Slaked lime | 1,628,678 |
| Solvent (makeup water) | 19,477 |
| Overhead | 97,230 |
| Taxes, insurance, administrative | 279,876 |
| Capital recovery | 768,223 |
| ------------------------------------------------- |  |
| Total Annual Cost | 3,168,241 |

Table 13. Costs of SO2 emission limits for 1,200,000 ton/yr kiln.*

| Option | 1 (Baseline) | 2 (1.33 lb/ton clinker) | 3 (0.4 lb/ton clinker) | 4 (0.2 lb/ton clinker) |
| --- | --- | --- | --- | --- |
| Capital cost High sulfur Moderate sulfur Low sulfur | 0 | $28,280,000 (WS) 0 0 | $28,280,000 (WS) $7,176,000 (DLS) 0 | $28,280,000 (WS) $28,280,000 (WS) 0 |
| Annualized cost High sulfur Moderate sulfur Low sulfur | 0 | $4,969,000 0 0 | $4,969,000 $3,224,000 0 | $4,969,000 $4,969,000 0 |
| Total SO2 reduction High sulfur Moderate sulfur Low sulfur | 0 | 7,410 tpy 0 0 | 7,410 tpy 540 tpy 0 | 7,410 tpy 741 tpy 0 |
| Total Cost Effectiveness High sulfur Moderate sulfur Low sulfur | 0 | 663 $/ton SO2 0 0 | 671 $/ton SO2 5,970 $/ton SO2 0 | 671 $/ton SO2 6,706 $/ton SO2 0 |

* Costs include monitoring costs.

WS = alkaline wet scrubber

DLS = lime injection

G. Summary of Impacts

Environmental and cost impacts for the proposed amendments on a model plant basis are summarized in Table 14. Nationwide impacts in the 5th year following promulgation are summarized in Table 15.

Table 14. Cost and environmental impacts of proposed amendments for a 1,200,000 ton/yr kiln.

| Pollutant | Cost ($)* | Emission Reduction (tpy) | Secondary Impacts |
| --- | --- | --- | --- |
|  | Capital | Annual |  | Increase in electricity demand (kWh/yr) | Increase in water usage (gpy) | Increase in solid waste (tpy) | Increase in emissions of NOx (tpy) | Increase in emissions of CO (tpy) | Increase in emissions of SO2 (tpy) | Increase in emissions of PM10 (tpy) |
| NOx | 2,289,000 | 1,268,000 | 600 | Negligible | 0 | 0 | 0 | 0 | 0 | 0 |
| PM | 1,428,000 | 211,000 | 44.4 | Negligible | 0 | 44.4 | 0 | 0 | 0 | 0 |
| SO2 | 28,280,000 | 4,969,000 | 7,410 | 12,075,355 | 97,000,000 | 84,101 | 26.9 | 13.9 | 46.2 | 1.4 |

*Includes monitoring costs.

Table 15. Nationwide cost and environmental impacts of proposed amendments.

| Pollutant | Cost ($)* | Emission Reduction (tpy) | Secondary Impacts |
| --- | --- | --- | --- |
|  | Capital | Annual |  | Increase in electricity demand (kWh/yr) | Increase in water usage (gpy) | Increase in solid waste (tpy) | Increase in emissions of NOx (tpy) | Increase in emissions of CO (tpy) | Increase in emissions of SO2 (tpy) | Increase in emissions of PM10 (tpy) |
| NOx | 45,800,000 | 25,400,000 | 12,000 | Negligible | 0 | 0 | 0 | 0 | 0 | 0 |
| PM | 28,600,000 | 4,200,000 | 890 | Negligible | 0 | 890 | 0 | 0 | 0 | 0 |
| SO2 | 113,000,000 | 19,900,000 | 29,640 | 48,301,000 | 388,000,000 | 336,400 | 108 | 56 | 185 | 5 |
| TOTAL | 187,400,000 | 49,500,000 |  |  |  |  |  |  |  |  |

*Includes monitoring cost.

H. References

Bahner, M. 2007. Review of Three BACT Analyses. October 10, 2007.

Bahner, M. 2008a. Review and Analysis of NOx Data for Four Cement Kilns. April 1, 2008.

Bahner, M. 2008b. Analysis of Particulate Matter Test Results:  2003 Survey, and Florida Kilns. March 31, 2008.

Bahner, M. 2008c. Summary of Cement Kiln Wet Scrubber and Lime Injection Design and Performance Data. May 2, 2008.

M. Bahner, and M. Laney 2008. Summary of Cement Kiln Wet Scrubber and Lime Injection Design and Performance Data, May 2, 2008.

CEMS Cost Model. CEMS.XLS. http://www.epa.gov/ttn/emc/cem.html. Accessed March, 2008.

Heath, E. 1996. Summary of Inputs of Control Options on Model Kilns and Clinker Cooler. Docket Item II-B-67, Docket A-92-53. April 19, 1996.

Florida Department of Environmental Protection (FL DEP). 2005. Technical Evaluation Preliminary Determination Draft BACT Determinations Sumter Cement Company, Sumter County, Florida, New Portland Cement Plant. DEP File No. 1190041-001-AC (PSD-FL-358). Available at: http://www.dep.state.fl.us/air/permitting/construction/sumter/TEPD358.pdf.

Laney, M., D. Green and K Barnett 2006. Summary of Environmental and Cost Impacts of Final Amendments to Portland Cement NESHAP, December 8, 2006, Docket item EPA-HQ-OAR-2002-0051-1891.

Northeast States for Coordinated Air Use Management (NESCAUM) in Partnership with the Mid-Atlantic/Northeast Visibility Union. 2005. Assessment of Control Technology Options for BART-Eligible Sources. Steam Electric Boilers, Industrial Boilers, Cement Plants and Paper and Pulp Facilities. March 2005.

Portland Cement Association. 2006. Capacity Expansion Estimates. October 13, 2006.

Portland Cement Association. 2007. U.S. and Canadian Portland Cement Industry Plant Information Summary December 31, 2006.

U.S. Environmental Protection Agency (EPA), 2007. Alternative Control Technologies Document Update - NOx Emissions from New Cement Kilns, November 2007.

US EPA. EPA Air Pollution Cost Control Manual: Sixth Edition: Section 6: Particulate Matter Controls: Chapter 1: Baghouses and Filters. Document Number EPA/452/B-02-001. December 1998.

U. S. Environmental Protection Agency 2002. Office of Air Quality Planning and Standards. EPA Air Pollution Control Cost Manual, Sixth Edition, EPA/452/B-02-001. January 2002.

U. S. Environmental Protection Agency, Office of Atmospheric Programs. Output-Based Regulations: A Handbook for Air Regulators. August, 2004.

United States Geological Survey. USGS 2006 Minerals Yearbook. Gypsum. Nov. 2007.

Zephyr Environmental Corporation. PSD Application for Lehigh Mason City. September 2002.

Attachment 1

SO2 Monitor Cost

Output from the EPA CEMS Cost Model

Attachment 1

| Summary of CEMS |  |  |  |  |
| --- | --- | --- | --- | --- |
| Analyzers |  | BEFORE | AFTER |  |
| CO |  | 0 | 0 |  |
| SO2 |  | 0 | 1 |  |
| NOX |  | 0 | 0 |  |
| HCl |  | 0 | 0 |  |
| Mercury (and CO2/O2) |  | 0 | 0 |  |
| CO2 |  | 0 | 0 |  |
| O2 |  | 0 | 0 |  |
| THC |  | 0 | 0 |  |
| Monitors |  |  |  |  |
| OPACITY |  | 0 | 0 |  |
| FLOW |  | 0 | 0 |  |
| PM (beta gauge) |  | 0 | 0 |  |
| PM (light scattering; insitu) |  | 0 | 0 |  |
| PM (light scattering; extractive) |  | 0 | 0 |  |
| Bag leak detector |  |  |  |  |
| Number of fabric filters to be monitored= |  | 0 | 0 |  |
| Number of sensors= |  | 0 | 0 |  |
| Summary of Costs |  |  |  |  |
| First Costs | Labor | Test | ODCs | Total |
| Planning | 2,534 | 0 | 352 | 2,886 |
| Select Equipment | 10,941 | 0 | 3,067 | 14,008 |
| Support Facilities | 0 | 0 | 19,065 | 19,065 |
| Purchase CEMS Hardware | 0 | 0 | 64,978 | 64,978 |
| Install and Check CEMS | 4,818 | 0 | 11,979 | 16,797 |
| Performance Specification Tests | 2,129 | 7,526 | 503 | 10,157 |
| QA/QC Plan | 2,570 | 11,981 | 692 | 15,244 |
|  | 22,993 | 19,507 | 100,635 | 143,135 |
| Annual Costs |  |  |  |  |
| Day-to-Day Activities | 5,532 | 0 | 1,000 | 6,532 |
| Annual RATA | 885 | 7,156 | 0 | 8,041 |
| PM Monitor RCA | 0 | 0 | 0 | 0 |
| PM Monitor RRA | 0 | 0 | 0 | 0 |
| Cylinder Gas Audits (ACA/SVA for PM) | 1,284 | 0 | 1,069 | 2,353 |
| Recordkeeping and Reporting | 1,253 | 0 | 160 | 1,413 |
| Annual QA & O&M Review and Update | 2,074 | 0 | 1,530 | 3,604 |
| Capital Recovery | 3,274 | 2,778 | 14,330 | 20,382 |
| Total w/o capital recovery | 11,029 | 7,156 | 3,759 | 21,944 |
| Total with capital recovery | 14,303 | 9,934 | 18,089 | 42,326 |

Attachment 2

NOx Monitor Cost

Output from the EPA CEMS Cost Model

Attachment 2

| Summary of CEMS |  |  |  |  |
| --- | --- | --- | --- | --- |
| Analyzers |  | BEFORE | AFTER |  |
| CO |  | 0 | 0 |  |
| SO2 |  | 0 | 0 |  |
| NOX |  | 0 | 1 |  |
| HCl |  | 0 | 0 |  |
| Mercury (and CO2/O2) |  | 0 | 0 |  |
| CO2 |  | 0 | 0 |  |
| O2 |  | 0 | 0 |  |
| THC |  | 0 | 0 |  |
| Monitors |  |  |  |  |
| OPACITY |  | 0 | 0 |  |
| FLOW |  | 0 | 0 |  |
| PM (beta gauge) |  | 0 | 0 |  |
| PM (light scattering; insitu) |  | 0 | 0 |  |
| PM (light scattering; extractive) |  | 0 | 0 |  |
| Bag leak detector |  |  |  |  |
| Number of fabric filters to be monitored= |  | 0 | 0 |  |
| Number of sensors= |  | 0 | 0 |  |
| Summary of Costs |  |  |  |  |
| First Costs | Labor | Test | ODCs | Total |
| Planning | 2,534 | 0 | 352 | 2,886 |
| Select Equipment | 10,941 | 0 | 3,067 | 14,008 |
| Support Facilities | 0 | 0 | 19,065 | 19,065 |
| Purchase CEMS Hardware | 0 | 0 | 62,794 | 62,794 |
| Install and Check CEMS | 4,818 | 0 | 11,979 | 16,797 |
| Performance Specification Tests | 2,129 | 7,526 | 502.5 | 10,157 |
| QA/QC Plan | 2,570 | 11,981 | 692 | 15,244 |
|  | 22,993 | 19,507 | 98,451 | 140,951 |
| Annual Costs |  |  |  |  |
| Day-to-Day Activities | 5,532 | 0 | 1,000 | 6,532 |
| Annual RATA | 885 | 7,156 | 0 | 8,041 |
| PM Monitor RCA | 0 | 0 | 0 | 0 |
| PM Monitor RRA | 0 | 0 | 0 | 0 |
| Cylinder Gas Audits (ACA/SVA for PM) | 1,284 | 0 | 1,069 | 2,353 |
| Recordkeeping and Reporting | 1,253 | 0 | 160 | 1,413 |
| Annual QA & O&M Review and Update | 2,074 | 0 | 1,324 | 3,398 |
| Capital Recovery | 3,274 | 2,778 | 14,019 | 20,071 |
| Total w/o capital recovery | 11,029 | 7,156 | 3,553 | 21,738 |
| Total with capital recovery | 14,303 | 9,934 | 17,572 | 41,809 |

Attachment 3

Flow Rate Monitor Cost

Output from the EPA CEMS Cost Model

Attachment 3

| Summary of CEMS |  |  |  |  |
| --- | --- | --- | --- | --- |
| Analyzers |  | BEFORE | AFTER |  |
| CO |  | 0 | 0 |  |
| SO2 |  | 0 | 0 |  |
| NOX |  | 0 | 0 |  |
| HCl |  | 0 | 0 |  |
| Mercury (and CO2/O2) |  | 0 | 0 |  |
| CO2 |  | 0 | 0 |  |
| O2 |  | 0 | 0 |  |
| THC |  | 0 | 0 |  |
| Monitors |  |  |  |  |
| OPACITY |  | 0 | 0 |  |
| FLOW |  | 0 | 1 |  |
| PM (beta gauge) |  | 0 | 0 |  |
| PM (light scattering; insitu) |  | 0 | 0 |  |
| PM (light scattering; extractive) |  | 0 | 0 |  |
| Bag leak detector |  |  |  |  |
| Number of fabric filters to be monitored= |  | 0 | 0 |  |
| Number of sensors= |  | 0 | 0 |  |
| Summary of Costs |  |  |  |  |
| First Costs | Labor | Test | ODCs | Total |
| Planning | 806 | 0 | 0 | 806 |
| Select Equipment | 1,709 | 0 | 293 | 2,002 |
| Support Facilities | 0 | 0 | 1,000 | 1,000 |
| Purchase CEMS Hardware | 0 | 0 | 19,080 | 19,080 |
| Install and Check CEMS | 1,037 | 0 | 690 | 1,727 |
| Performance Specification Tests | 77 | 440 | 0 | 517 |
| QA/QC Plan | 2,306 | 7,650 | 692 | 10,647 |
|  | 5,934 | 8,090 | 21,755 | 35,780 |
| Annual Costs |  |  |  |  |
| Day-to-Day Activities | 691 | 0 | 0 | 691 |
| Annual RATA | 0 | 0 | 0 | 0 |
| PM Monitor RCA | 0 | 0 | 0 | 0 |
| PM Monitor RRA | 0 | 0 | 0 | 0 |
| Cylinder Gas Audits (ACA/SVA for PM) | 0 | 0 | 0 | 0 |
| Recordkeeping and Reporting | 5,448 | 0 | 40 | 5,488 |
| Annual QA & O&M Review and Update | 1,409 | 0 | 1,180 | 2,589 |
| Capital Recovery | 845 | 1,152 | 3,098 | 5,095 |
| Total w/o capital recovery | 7,548 | 0 | 1,220 | 8,768 |
| Total with capital recovery | 8,394 | 1,152 | 4,318 | 13,864 |

Attachment 4

Bag Leak Detector Cost

Output from the EPA CEMS Cost Model

Attachment 4

| Summary of CEMS |  |  |  |  |
| --- | --- | --- | --- | --- |
| Analyzers |  | BEFORE | AFTER |  |
| CO |  | 0 | 0 |  |
| SO2 |  | 0 | 0 |  |
| NOX |  | 0 | 0 |  |
| HCl |  | 0 | 0 |  |
| Mercury (and CO2/O2) |  | 0 | 0 |  |
| CO2 |  | 0 | 0 |  |
| O2 |  | 0 | 0 |  |
| THC |  | 0 | 0 |  |
| Monitors |  |  |  |  |
| OPACITY |  | 0 | 0 |  |
| FLOW |  | 0 | 0 |  |
| PM (beta gauge) |  | 0 | 0 |  |
| PM (light scattering; insitu) |  | 0 | 0 |  |
| PM (light scattering; extractive) |  | 0 | 0 |  |
| Bag leak detector |  |  |  |  |
| Number of fabric filters to be monitored= |  | 0 | 2 |  |
| Number of sensors= |  | 0 | 10 |  |
| Summary of Costs |  |  |  |  |
| First Costs | Labor | Test | ODCs | Total |
| Planning | 1,711 | 0 | 352 | 2,063 |
| Select Equipment | 6,346 | 0 | 643 | 6,989 |
| Support Facilities | 0 | 0 | 3,950 | 3,950 |
| Purchase CEMS Hardware | 0 | 0 | 66,568 | 66,568 |
| Install and Check CEMS | 484 | 0 | 12,927 | 13,411 |
| Performance Specification Tests | 0 | 0 | 0 | 0 |
| QA/QC Plan | 739 | 0 | 0 | 739 |
|  | 9,279 | 0 | 84,440 | 93,719 |
| Annual Costs |  |  |  |  |
| Day-to-Day Activities | 2,822 | 0 | 0 | 2,822 |
| Annual RATA | 0 | 0 | 0 | 0 |
| PM Monitor RCA | 0 | 0 | 0 | 0 |
| PM Monitor RRA | 0 | 0 | 0 | 0 |
| Cylinder Gas Audits (ACA/SVA for PM) | 0 | 0 | 0 | 0 |
| Recordkeeping and Reporting | 946 | 0 | 0 | 946 |
| Annual QA & O&M Review and Update | 384 | 0 | 17,250 | 17,634 |
| Capital Recovery | 1,321 | 0 | 12,024 | 13,346 |
| Total w/o capital recovery | 4,152 | 0 | 17,250 | 21,402 |
| Total with capital recovery | 5,473 | 0 | 29,274 | 34,748 |

Attachment 5

Statistical Analyses of Cement Kiln PM Data

PH/PC Kilns built since 1997-Fabric Filters with Membrane Bags

Attachment 5

| Statistical Analyses of Cement Kiln PM Data |
| --- |
| PH/PC Kilns built since 1997-Fabric Filters with Membrane Bags |
|  |  | PM Emissions | Conversion Factor | PM Emissions |
| Facility Name | Emissions Point | (gr.dscf) |  | lb/ton clinker |
| Ash Grove, Chanute | Kiln, December 4, 2003 | 0.0051 | 12.72 | 0.0649 |
| Ash Grove, Chanute | Kiln, December 5, 2003 | 0.00072 | 12.72 | 0.0092 |
| Ash Grove, Chanute | Kiln, September 8, 2004 | 0.0022 | 12.72 | 0.0280 |
| Ash Grove, Chanute | Kiln, September 9, 2004 | 0.0007 | 12.72 | 0.0089 |
| Ash Grove, Chanute | Kiln, November 15, 2005 | 0.0074 | 12.72 | 0.0941 |
| Ash Grove, Chanute | Kiln, November 15, 2005 | 0.008 | 12.72 | 0.1018 |
| Ash Grove, Chanute | Kiln, November 15, 2005 | 0.0026 | 12.72 | 0.0331 |
| Ash Grove, Chanute | Kiln, November 16, 2005 | 0.0042 | 12.72 | 0.0534 |
| Ash Grove, Chanute | Kiln, November 16, 2005 | 0.0031 | 12.72 | 0.0394 |
| Ash Grove, Chanute | Kiln, November 16, 2005 | 0.0032 | 12.72 | 0.0407 |
| Ash Grove, Chanute | Kiln, November 17, 2005 | 0.0025 | 12.72 | 0.0318 |
| Ash Grove, Chanute | kiln, November 17, 2005 | 0.001 | 12.72 | 0.0127 |
| Ash Grove, Chanute | Kiln, November 17, 2005 | 0.0016 | 12.72 | 0.0204 |
| Lehigh Cement, Union Bridge, MD | Kiln (Mill On) |  |  | 0.0023 |
| Lehigh Cement, Union Bridge, MD | Kiln (Mill Off) |  |  | 0.0045 |
| Lafarge Cement, Sugar Creek, MO | Kiln (Mill On) |  |  | 0.0046 |
| Lafarge Cement, Sugar Creek, MO | Kiln (Mill Off) |  |  | 0.0317 |
| Holcim, Devil's Slide, UT | Kiln, Mill On (October 2002) |  |  | 0.0391 |
| Holcim, Devil's Slide, UT | Kiln, Mill Off (October 2002) |  |  | 0.0584 |
|  |  |  | Minumim | 0.0023 |
|  |  |  | Maximum | 0.10176 |
|  |  |  | Average | 0.035732126 |
|  |  |  | Standard Deviation | 0.028721542 |
|  |  |  | 99th Percertile | 0.102538433 |
|  |  |  | 95th Percentile | 0.082979063 |
|  |  |  | Median | 0.0318 |