February 2008

Procurement Specification for Direct User Access Terminal (DUAT) Service

Flight Services Program Operations

Federal Aviation Administration

800 Independence Avenue, SW

Washington, DC 20591

Change Record

| Change Letter | Description of Change | Date | Changed By | Approved By |
| --- | --- | --- | --- | --- |

TABLE OF CONTENTS

1.0 SCOPE	7

1.1	Identification	7

1.2 System Overview	7

1.3 Document Overview	7

2.0 APPLICABLE DOCUMENTS	8

2.1 Sources of Documents	8

2.1.1 Sources of FAA, Military and Federal Documents	8

2.2.3 Sources of Other Documents	9

2.2.3.1  Sources of International Telecommunication Union (ITU) Documents:	9

ITU Documents may be obtained from their Website at http://www.itu.int/publications or from phone: +41 22 730 5111.  The ITU’s address is:	9

2.2.3.2  Sources of ICAO Documents	9

3.0 REQUIREMENTS	10

3.1 Definition	10

3.2.1 Functional Characteristic	10

3.2.1.1 General Requirements	11

3.2.1.1.1 Data Entry and Formats	12

3.2.1.1.2 Airport Diagrams	12

3.2.1.1.3  Military Graphical Data	12

3.2.1.2 Range of Service	12

3.2.1.2.1 Weather Briefing and Flight Planning	12

3.2.1.2.1.1 Reserved	12

3.2.1.2.2 International Weather Support	12

3.2.1.3	Source Data and Database Maintenance	13

3.2.1.3.1	Authorized Users	13

3.2.1.3.1.1     Graphic Weather Data	13

3.2.1.3.2	Static Flight Data	14

3.2.1.3.2.1	Data Availability	14

3.2.1.3.2.2	Editing and Error Correction	14

3.2.1.3.2.3	Characteristics	14

3.2.1.3.3	Dynamic Weather and NOTAM Data	14

3.2.1.3.3.1	Weather and NOTAM Products	15

3.2.1.3.3.1.1	Full Text Products	15

3.2.1.3.3.2	ICAO Weather Codes	15

3.2.1.3.3.3	Surface Weather Observations	15

3.2.1.3.3.4	Data Retention	15

3.2.1.3.3.4.1	Data Purge	15

3.2.1.3.3.5	Corrected or Amended Weather Products	16

3.2.1.3.3.6  Reserved	16

3.2.1.3.3.7  Routine Delay Weather Products	16

3.2.1.4	Processing Requirements	16

3.2.1.4.1	Database Maintenance	16

3.2.1.4.1.1	Alphanumeric Weather Data	16

3.2.1.4.1.2	Reserved	16

3.2.1.4.1.3  Static Flight Data	16

3.2.1.4.1.4	User Directory Assistance	17

3.2.1.4.2	Weather Message Identification	17

3.2.1.4.2.1	Weather Message Text Editing	17

3.2.1.4.2.2	Weather Message Duplication	17

3.2.1.4.3  Weather Information Function	17

3.2.1.4.3.1	Weather Briefing Formats	17

3.2.1.4.3.1.1	Standard Weather Briefing	18

3.2.1.4.3.1.1.1	Input	18

3.2.1.4.3.1.1.2	Output	19

3.2.1.4.3.1.2	Abbreviated Weather Briefing	19

3.2.1.4.3.1.2.1	Input	19

3.2.1.4.3.1.2.2	Output	20

3.2.1.4.3.1.3	Outlook Weather Briefing	20

3.2.1.4.3.1.3.1	Input	20

3.2.1.4.3.1.3.2	Output	20

3.2.1.4.3.2  Adverse Weather Products	21

3.2.1.4.3.2.1	Standard and Outlook Weather Briefing	21

3.2.1.4.3.2.1.1	Tropical Advisories	21

3.2.1.4.3.2.1.2	Reserved	21

3.2.1.4.3.2.1.3	Severe Weather Outlook	21

3.2.1.4.3.2.2	Abbreviated Weather Briefing	21

3.2.1.4.3.2.3  Area Forecast Output	21

3.2.1.4.3.3	Trend Weather Products	21

3.2.1.4.3.3.1	Trend Weather Product Requests	22

3.2.1.4.3.4	Forecast Winds and Temperatures Aloft	22

3.2.1.4.3.4.1	Output Time Period	22

3.2.1.4.3.5	Alternate Airport Weather	22

3.2.1.4.3.6	Closest Reporting Location	22

3.2.1.4.3.7	Collective Products	23

3.2.1.4.3.8	Weather Briefing Entry Carryover	23

3.2.1.4.3.9	Use of Previous Route	23

3.2.1.4.3.10  Reserved	23

3.2.1.4.3.11	Product Retrieval	23

3.2.1.4.3.11.1	Weather Product Search Area	23

3.2.1.4.3.11.2	Retrieval Processing	23

3.2.1.4.3.12	NOTAMs	23

3.2.1.4.3.12.1	Non-associated Facilities	23

3.2.1.4.3.12.2	Reserved	24

3.2.1.4.3.13   Graphic TFRs	24

3.2.1.4.3.14   Superseded Products	24

3.2.1.4.3.15  DUAT Service Interruptions	24

3.2.1.4.3.15.1   Short-Term Weather Data Interruption	24

3.2.1.4.3.15.1.1    Short-Term Interruption Message	24

3.2.1.4.3.15.1.2   Short-Term Interruption Resumption	25

3.2.1.4.3.15.2   Long-Term Weather Data Interruption	25

3.2.1.4.3.15.2.1  Long-Term Interruption Message	25

3.2.1.4.3.15.2.2  Long-Term Interruption Resumption	25

3.2.1.4.3.15.3   USNS-R Interruption	25

3.2.1.4.3.15.4   DUAT Service System Failure	25

3.2.1.4.3.15.4.1   DUAT Data Base Rebuild	26

3.2.1.4.3.15.4.2  DUAT System Failure Message	26

3.2.1.4.3.16  Unavailable Weather Products	26

3.2.1.4.3.16.1   Product Not in the Database	26

3.2.1.4.3.16.2   Invalid Product	26

3.2.1.4.3.16.3  Invalid Format	26

3.2.1.4.4  Flight Planning Function	26

3.2.1.4.4.1	Flight Planning Software Capabilities	27

3.2.1.4.4.2	Stored Flight Plans	27

3.2.1.4.4.3	Message Formatting`	27

3.2.1.4.4.3.1	Flight Data Message Precedence	27

3.2.1.4.4.4	Flight Plan Processing	27

3.2.1.4.4.4.1	Domestic Flight Plan Processing	28

3.2.1.4.4.4.2	ICAO Flight Plan Processing	28

3.2.1.4.4.4.3	Adverse Weather Conditions	28

3.2.1.4.4.5	Acknowledgments	28

3.2.1.4.4.6	IFR Flight Plans	28

3.2.1.4.4.6.1	IFR Parameter Time	28

3.2.1.4.4.7	Domestic and ICAO VFR Flight Plans	29

3.2.1.4.4.7.1	Domestic and ICAO VFR Parameter Time	29

3.2.1.4.4.8	Alaska Flight Plans	29

3.2.1.4.4.9	File Flight Plan with ARTCC	29

3.2.1.4.4.10	Multiple Flight Plans	29

3.2.1.4.4.10.1	Dispatcher Flight Plans	29

3.2.1.4.4.11	Formatted Flight Plans	29

3.2.1.4.4.12	Data Transmission	30

3.2.1.4.4.13	Flight Plan Storage	30

3.2.1.4.4.13.1	IFR Flight Plan Storage	30

3.2.1.4.4.13.2	VFR Flight Plan Storage	30

3.2.1.4.4.14	Time Modifications	30

3.2.1.4.4.15	Duplicate Flight Plans	30

3.2.1.4.4.16	Flight Plan Acknowledgments	30

3.2.1.4.4.16.1  IFR Acknowledgment	30

3.2.1.4.4.16.2  VFR Acknowledgment	31

3.2.1.4.4.17	Error/Reject Messages	31

3.2.1.4.4.17.1	Error Message Procedures	31

3.2.1.4.4.17.2	Reject Message Procedures	31

3.2.1.4.4.18	Flight Plan Filing	32

3.2.1.4.4.19	Lifeguard Flights	32

3.2.1.4.4.20	Flight Plan Input	32

3.2.1.4.4.20.1	Domestic Flight Plan Acceptance	32

3.2.1.4.4.20.2	ICAO Flight Plan Acceptance	32

3.2.1.4.4.20.3	Incorrect Entries	32

3.2.1.4.4.20.4	Format Checking	32

3.2.1.4.4.20.5	Latitude-Longitude Entry	33

3.2.1.4.4.20.6	Washington, DC Metropolitan Area Flight Restricted Zone (DC FRZ)	33

3.2.1.4.4.21	Flight Plan Display	33

3.2.1.4.4.21.1	Flight Plan Modification/Filing	33

3.2.1.4.4.21.1.1	Weather Briefing Update	33

3.2.1.4.4.21.1.2	Re-output Modified Flight Plan	33

3.2.1.4.4.21.1.3	Continuation of Changes	33

3.2.1.4.4.22	Completion Message	33

3.2.1.4.4.23	Reserved	34

3.2.1.4.4.24	Route Definition	34

3.2.1.4.4.24.1	Valid Elements and Fixes	34

3.2.1.4.4.24.2	Route Contiguous Legs	34

3.2.1.4.4.24.3	Previously Entered Data	34

3.2.1.4.4.24.4	Preferred Routes	34

3.2.1.4.4.24.4.1	Preferred Route Selection	35

3.2.1.4.4.25	Flight Plan Amendments/Cancellations	35

3.2.1.4.4.25.1	Authorization	35

3.2.1.4.4.25.2	Flight Plan Retrieval	35

3.2.1.4.4.25.3	Flight Plan Amendments	35

3.2.1.4.4.25.3.1	Flight Plan Time Limits	35

3.2.1.4.4.26	Flight Plan Entry Carryover	35

3.2.1.4.4.27	Acceptance Messages	35

3.2.1.4.4.28  Cancel Flight Plans	36

3.2.1.4.4.28.1	Flight Plan Retention	36

3.2.1.4.4.28.2	Time for Cancellation	36

3.2.1.4.4.28.3	Message After Cancellation	36

3.2.1.4.4.28.4	Notification of Transmission	36

3.2.1.4.4.28.5	No Flight Plan Message	36

3.2.1.4.4.29	VFR Flight Plan Closure	36

3.2.1.4.4.29.1	Flight Plan Closure Acceptance	36

3.2.1.4.4.29.1.1	Required Entries	36

3.2.1.4.4.29.2	Closure Message	37

3.2.1.4.4.29.3	Receipt of Closure Message	37

3.2.1.4.4.29.4	Acknowledgment	37

3.2.1.4.4.30	Traffic Management Function	37

3.2.1.4.4.31	Encode/Decode Functions	37

3.2.1.4.4.31.1	Domestic Location Information	38

3.2.1.4.4.31.2	ICAO Area of Responsibility	38

3.2.1.4.4.32	Escape to Encode/Decode Function	38

3.2.1.4.4.33	Data Recording and Retention	38

3.2.1.4.4.33.1	Event Recording and Reconstruction	38

3.2.1.4.4.33.1.1	Transaction Recording	38

3.2.1.4.4.33.1.2	Event Reconstruction	39

3.2.1.4.4.33.1.2.1	Event Retrieval Key	39

3.2.1.4.4.33.1.2.2	Event Retrieval Time Period	39

3.2.1.4.4.33.1.3	Transaction Data Retention	39

3.2.1.4.4.33.2	Incoming Weather and NOTAM Data	39

3.2.1.4.4.33.2.1	Weather and NOTAM Data Recording	40

3.2.1.4.4.33.2.2	Weather and NOTAM Data Retention	40

3.2.1.4.4.33.2.3	Data Retrieval	40

3.2.1.4.4.33.2.3.1	Time-Stamp Display	40

3.2.1.4.4.33.3	Event Reconstruction Requests	40

3.2.1.4.4.33.3.1	Request Response Time	41

3.2.1.4.4.34	Search and Rescue Requests (SAR)	41

3.2.1.4.4.34.1	SAR Response Time	41

3.2.1.4.4.34.2	SAR Response Order	41

3.2.1.4.4.34.3	Data Search	41

3.2.1.4.4.34.3.1	Continuation of Search	41

3.2.1.4.4.34.4	Data Retrieval	41

3.2.1.4.4.34.5	Response Data	42

3.2.1.4.4.34.6	No Data Found in Search	42

3.2.1.4.5	DUAT Service Access	42

3.2.1.4.5.1	Transaction Provisions	42

3.2.1.4.5.1.1	Time Recording Accuracy	42

3.2.1.4.5.1.2	User Time Warnings	43

3.2.1.4.5.2	Termination	43

3.2.1.4.5.2.1	Transaction Termination	43

3.2.1.4.5.2.2	Time-out Termination	43

3.2.1.4.5.2.2.1	Time-out	43

3.2.1.4.5.2.2.2   Reserved	43

3.2.1.4.5.2.2.3  Termination Disconnect	43

3.2.1.4.5.3	Transaction Number	43

3.2.1.4.5.3.1	Sequence Assignment	43

3.2.1.4.5.3.2	Storage	43

3.2.1.4.6	User Information	44

3.2.1.4.6.1	FAA Information	44

3.2.1.4.6.2	Input Error Detection	44

3.2.1.4.6.2.1	Reentering Data	44

3.2.1.4.6.3	Date and Time Display	44

3.2.1.4.7	Help Function	44

3.2.1.4.7.1	Help Function Field Entries	44

3.2.1.4.7.2	Access to Help Function	44

3.2.1.4.7.3	Expanded Help Function	44

3.2.1.4.7.4.  ICAO Help Function	45

3.2.1.4.7.4.1	ICAO Help Function Entry	45

3.2.1.4.8	DUAT Service Help Line	45

3.2.1.5	Interface Requirements	45

3.2.1.5.1	Reserved	45

3.2.1.5.1.1	Reserved	45

3.2.1.5.1.2	Reserved	45

3.2.1.5.1.3	Reserved	45

3.2.1.5.1.4	Interface with NAS Systems	45

3.2.1.5.1.4.1	Reserved	46

3.2.1.5.1.5	Atomatic Call Detection	46

3.2.1.5.1.6	Call-Termination	46

3.2.1.5.2	DUAT TCP/IP Interfaces	46

3.2.1.5.2.1	NAS Messages	46

3.2.1.5.2.1.1	Originator's Address	46

3.2.1.5.2.1.2	Data Exchanges	47

3.2.1.6	Performance Requirements	47

3.2.1.6.1	Simultaneous Users	47

3.2.1.6.2	Time Source Synchronization	47

3.2.1.6.3	Flight Plan Error Rate	48

3.2.1.6.4  Qualified Internet Communications Provider (QICP) Requirement	48

3.2.2     Reserved	49

3.2.3	System Quality Factors	49

3.2.3.1	Reliability	49

3.2.3.2	Maintainability	49

3.2.3.3	Availability	49

3.2.4	System Flexibility and Growth	49

3.2.4.1	DUAT Service User Growth	49

3.3       Reserved	49

3.3.1	Human Engineering	49

3.3.1.1	Human Factors	50

3.3.1.1.1	Command Language	50

3.3.1.1.2	User Feedback	50

3.3.1.1.2.1	Feedback Message	50

3.3.1.1.2.1.1	Feedback Time	50

3.3.1.1.2.2	Error Messages	50

3.3.1.1.2.2.1	Command Response Message	50

3.3.1.1.2.2.2	Command Error Message	51

3.3.2	through 3.3.9 Reserved	51

3.3.9.1	General Security Requirements	51

3.3.9.1.1	Physical Security	51

3.3.9.1.2	Telecommunications and Information Security	51

3.3.9.1.3	User Passwords	51

3.3.9.2	Access Levels	51

3.3.9.2.1	Weather Briefing/Flight Planning Access	51

3.3.9.2.2	Authorized Users Database Access	52

3.3.9.2.3	User Information Display Area Access	52

3.3.9.3	Reserved	52

3.3.9.4	Access Restrictions	52

3.3.9.5	Initial Access Validation	52

3.3.9.5.1	Access Non-Validation	52

3.3.9.5.1.1	New DUAT User Access	52

3.3.9.5.1.1.1	Documentation Retention	52

3.3.9.6	Access Code and Password Assignment	53

3.3.9.6.1	Access Codes	53

3.3.9.6.1.1	Access Security	53

3.3.9.6.1.2	Password	53

3.3.9.6.2	Retention for Future Use	53

3.3.9.7	Log-on	53

3.3.9.7.1	Log-on Denial	53

3.3.9.7.1.1	Log-on Denial Remarks	53

3.3.9.7.2	Record of Log-on Attempts	54

3.3.9.8	Scope of the Information Systems Security Program	54

3.3.9.8.1  Security Implementation	54

3.3.9.8.2  Security Responsibilities	54

4.0   rESERVED	54

5.0   Acronyms, Definitions, Glossary	54

Figures & Tables

| Number | Title | Page |
| --- | --- | --- |
| Figure 3.1-1 | DUAT Service System Diagram | 10 |
| Table 3.2.1.4.3.1-1 | Weather Briefing Types | 18 |
| Table 3.2.1.6-1 | Processing Performance Requirements | 48 |
| Table 3.2.1.6-2 | Data Performance Requirements | 48 |
| Table A | Static Flight Data | A-1 |
| Table B | Adaptable Parameters | B-1 |
| Table E | DUAT Service VRTM | E-1 |

Appendices

| Appendix | Title | Page |
| --- | --- | --- |
| Appendix A | Static Flight Data | A-1 |
| Appendix B | Adaptable Parameters | B-1 |
| Appendix C | Product Listing | C-1 |
| Appendix D | Reserved | D-1 |
| Appendix E | Verification Requirements Traceability Matrix (VRTM) | E-1 |

# 1.0 SCOPE

## Identification

This specification sets forth the functional and performance requirements for Direct User Access Terminal (DUAT) Service.  To facilitate traceability, individual requirements have been assigned unique identification numbers encased in brackets (e.g., [000]).   Appendix E to this specification contains a cross reference between specification paragraphs and identification numbers.  References to Automated Flight Service Stations (AFSSs) and Flight Service Stations (FSSs) within the specification apply equally to both types of activities.

## 1.2 System Overview

DUAT Service is an Internet-based weather information and flight plan processing service provided by the Federal Aviation Administration (FAA) through designated Service Providers for United States civil aviation pilots and other authorized users.  It allows pilots to use personal computers or remotely connected computer terminals to access an FAA database to obtain weather and aeronautical information, to file, amend, and cancel flight plans, and to close Visual Flight Rules [VFR] flight plans. Pilots can connect to the DUAT Service low-speed (ASCII) interface via a communications circuit providing toll free telephone numbers or to the high-speed interface using popular Internet web-browsers.

Major DUAT Service functions include the capabilities to:

(a) Provide a selection of weather information formats (standard, abbreviated or outlook) for routes or defined areas,

(b) Process flight plans and associated messages,

(c) Encode/decode location names and location identifiers (LOCIDs),

(d) Provide select weather graphic products,

(e)  Provide information services to FAA offices, and

(f)  Ensure that the security of the NAS is not compromised by the delivery of DUAT Service.

## 1.3 Document Overview

This document is organized as follows:

Section 1.  This section includes the scope of the document.

Section 2.  This section identifies documents applicable to this specification.

Section 3.  This section includes the DUAT Service functional, performance and interface requirements.

Section 4.  Reserved.

Section 5.  This section identifies where an acronym list, definitions, and a glossary can be found.

# 2.0 APPLICABLE DOCUMENTS

The documents identified in Section J3 “Applicable Documents” of the DUAT Schedule form a part of this specification to the extent specified herein.  The version of each document in effect on the date of the release of the Screening Information Request is the version that applies to all requirements.

## 2.1 Sources of Documents

### 2.1.1 Sources of FAA, Military and Federal Documents

The National Airspace System (NAS) Documentation Control Center (DCC) is the principal repository for NAS Configuration data and baselined documentation.  Points of Contact for the DCC are:

| U.S. Mail Address: | Physical Location |
| --- | --- |
| Federal Aviation Administration 800 Independence Avenue, S.W. Room 700W, AJW-27 ATTN: NAS Documentation Control Center (DCC) Washington, DC 20591 | 600 Maryland Avenue, S.W. Suite 700 Washington, DC 20024 Phone and Fax Numbers (202) 548-5502 (voice mail) (202) 548-5501 (Fax) |

Document Drop-off and Pickup by Appointment Only; 8:00 a.m. to 4:00 p.m. (ET)

The DCC maintains an index, inventory, and storage for NAS related information including specifications, FAA Standards, and NAS interface documents.  The DCC is the primary source within the FAA for the distribution of FAA Specifications, FAA Standards, Interface Requirement Documents (IRDs), and Interface Control Documents (ICDs).   Documents may be ordered directly off the DCC Website, which is accessible through http://www.faa.gov/cm by clicking on the “Document Control Center” topic.

Some FAA Advisory Circulars (ACs) and some FAA Orders are available from the Regulatory and Guidance Library website at http://rgl.faa.gov.  National Institute of Standards and Technology (NIST) documents may be obtained from its website at http://csrc.nist.gov/ publications/nistpubs or by phone at (301) 975-6478.   The NIST address is:

The National Institute of Standards & Technology (NIST)

100 Bureau Drive

Stop 1070

Gaithersburg, MD  20899-1070

### 2.2.3 Sources of Other Documents

Technical society and technical association specifications and standards are generally available for reference from libraries.  They are also distributed among technical groups and using Federal agencies.

#### 2.2.3.1  Sources of International Telecommunication Union (ITU) Documents:

#### ITU Documents may be obtained from their Website at http://www.itu.int/publications or from phone: +41 22 730 5111.  The ITU’s address is:

International Telecommunication Union (ITU)

Place des Nations

1211 Geneva 20

Switzerland

Note: Time in Switzerland is six (6) hours later than the East Coast Time Zone.

#### 2.2.3.2  Sources of ICAO Documents

Copies of International Civil Aviation Organization (ICAO) documents may be requested from ICAO’s Website  (http://www.icao.int/fsix) or from (514) 954-8022.    The ICAO’s address is:

Document Sales Unit

International Civil Aviation Organization

999 University Street

Montreal, Quebec

Canada H3C 5H7

Payment is required.

# 3.0 REQUIREMENTS

## 3.1 Definition

DUAT Service is a real-time, multi-user, computer-based system that functions in direct response to user requests for aviation weather information and flight plan processing.  An overview diagram indicating the functions and interfaces is shown in Figure 3.1-1, below.

3.2 Characteristics

### 3.2.1 Functional Characteristic

The DUAT Service must provide:

(a) Current weather information, [001]

(b) Forecast weather information, [002]

(c) Notice to Airmen (NOTAM) [003] information,

(d) Flight planning service [004] to authorized users,

(e)  Event reconstruction data to authorized FAA offices, and

(f)  An online help function.

DUAT Service must be available [005] 24 hours a day, 7 days a week.  It must [006] permit pilot users to connect to the service using toll free telephone numbers, or, at each pilot’s discretion, through the use of popular Internet web-browsers. [810]

#### 3.2.1.1 General Requirements

The SP’s DUAT Service must be capable of performing the following functions concurrently:

- Automatically accept, process, and store meteorological and aeronautical information received from the Weather Message Switching Center Replacement (WMSCR) or other comparable system or service; [007]

- Accept and process requests from multiple users for DUAT Service functions simultaneously; [008]

- File, amend, and cancel domestic and ICAO Instrument Flight Rule (IFR), domestic and ICAO Visual Flight Rule (VFR) flight plans originating in the contiguous United States, Alaska, Hawaii, Puerto Rico and the U.S. Virgin Islands; [009]

- Close domestic VFR Flight Plans; [010]

- Accept, process, and file flight plan information and interface with Air Route Traffic Control Centers (ARTCCs), Automated Flight Service Stations (AFSSs), and Flight Service Stations (FSSs); [011]

- Automatically address flight plans; [012]

- Store and retrieve data for each transaction; [013]

- Provide weather and NOTAM information to users, including user-defined weather product collectives; [014]

- Provide Event Recording and Reconstruction processing; [015]

- Provide Data Retrieval for Search and Rescue; [016]

- Provide System Security; [017]

- Provide Activity Reports; [018]

- Provide Encode and Decode functions; [019]

- Meet Availability Requirements; [020]

- Provide flow control and air traffic advisory/delay information (unscheduled reports received from ATCSCC/Advisory); [021]

- Provide information on airspace use and warning areas (unscheduled reports received from ATCSCC/Advisory). [022]    Provide users on-screen User Help Functions; [023]

- Provide users the capability to set-up, examine, retain, and modify individual adaptation and user profiles; [024]

- Maintain and report System Activity Statistics; [025]

- Provide a 24-hour a day user Help Line; [026]

- Accept and process requests from multiple users from Internet for DUAT Service functions simultaneously; [811] and

- Provide pilots the capability to access airport diagrams when using DUAT Service for pre-flight briefings. [812]

#### 3.2.1.1.1 Data Entry and Formats

Unless specifically stated otherwise in this specification, all required input, output, and display formats are design options.  The DUAT Service SP must [705] ensure that contractions adopted for user transactions are in accordance with FAA Order 7340.1.  References in this specification to user “data entry” refer to keyboard entries, menu selections, and web page links; whichever is appropriate for the function being executed.

#### 3.2.1.1.2 Airport Diagrams

In order to provide pilots with the capability to access towered airport diagrams for pre-flight briefings the DUAT Service SP must [706] include the following link and statement on its Web page:

"For airport/s familiarization, the following Website is available for airport diagrams: http://www.naco.faa.gov.  Not all airport diagrams are available at this time.”

#### 3.2.1.1.3  Military Graphical Data

DUAT Service must [920] use the FAA’s Aeronautical Information Service (AIS) data file, National Airspace System Resources, for Military Graphical Data.

#### 3.2.1.2 Range of Service

#### 3.2.1.2.1 Weather Briefing and Flight Planning

The DUAT Service must provide weather information services to users in the contiguous United States], Alaska, Hawaii, Puerto Rico, the US Virgin Islands, Mexico, Canada, and other briefing areas as appropriate. [027].

The DUAT Service must provide flight planning services to users in the contiguous United States , Alaska, Hawaii, Puerto Rico, and the US Virgin Islands in accordance with FAA Order 7110.10 [028].

#### 3.2.1.2.1.1 Reserved

#### 3.2.1.2.2 International Weather Support

DUAT Service must request weather information from the Weather Message Switching Center Replacement (WMSCR) or other comparable system or service when requested by users for the following areas.

(a) Canada, [029]

(b) Mexico, [030]

(c) Bahamas, [031]

(d) Puerto Rico, [032]

(e) Haiti, [033]

(f) Dominican Republic, [034]

(g) Virgin Islands, [035] and the

(h) Cayman Islands. [036]

The DUAT Service must provide the current surface observation(s) (including specials) [037], and terminal forecast(s) [038] for the international destinations above including alternate airports.

In conformance with  FAA Order 7110.10, Flight Services Handbook, paragraph 3-2-1, the DUAT Service must [750] provide the following cautionary statement to pilots planning flights outside of United States controlled airspace:  “Check data as soon as practical after entering foreign airspace, as our international data may be inaccurate or incomplete.”

#### Source Data and Database Maintenance

This section identifies the data and database maintenance requirements for the operation of the DUAT Service.  The four types of DUAT Service data are Airmen File Data, Static Flight Data, System Activity Statistics, and Dynamic Weather and NOTAM Data.

#### Authorized Users

The DUATS must [041] maintain a user database containing information from the FAA’s Airmen Certification database and any other users authorized by the FAA.

#### 3.2.1.3.1.1     Graphic Weather Data

The DUAT Service must receive [070] and maintain [072] a dynamic weather database using graphic weather products received from an FAA-approved source.

When graphic products are requested by the user, the DUAT Service must make available, but not necessarily be limited to, the following analysis, prognosis, and data products:

- Surface Analysis, [910]

- Weather Depiction, [911]

- National Radar Summary, [912]

- Forecast Winds Aloft, [923]

- Current Winds Aloft, [924]

- Constant Pressure Charts [925]

- 850 MB

- 700 MB

- 500 MB

- 300 MB

- 200 MB,

- Composite Moisture Stability Chart (Lifted Index, Precipitable Water, Freezing Level-Mean Relative Humidity), [915]

- 12- and 24-hour low level significant weather prognosis, [913]

- High level significant weather prognosis, [914]

- 36- and 48-hour surface prognosis, [926]

- Satellite Imagery Products, [927] and

- NEXRAD Products. [928]

The DUAT Service must [929] provide these products from an FAA approved source [813]. The minimum dimensions for the display of graphic weather data must [930] be 640 X 480 pixels, except when 4-Panel display format is being utilized.  All 4-Panel displays must [931] have an overall dimension at least 800 X 600 pixels with each individual quarter panel being at least 360 X 270 pixels.

#### Static Flight Data

The DUAT Service must use Static Flight Data to support dynamic weather [042] and NOTAM [043] data processing and flight planning [044] functions (See Appendix A).

#### Data Availability

The DUAT Service must [045] update Static Flight Data and make them available for processing on the effective date of the data.

#### Editing and Error Correction

The DUAT Service must [046] have the capability for on-site correction of errors that may exist in the Static Flight Data.  The DUATS must [047] correct errors in the Static Flight Data using all available means including, but not limited to, sources described in paragraph 3.2.1.4.1.3 and notify the FAA as soon as possible.

#### Characteristics

Identification, source, and characteristics of the Static Flight Data must [048] be as specified in Appendix A.

#### Dynamic Weather and NOTAM Data

The DUATS must [049] use WMSCR or a comparable system or service for all weather and NOTAM data.  If WMSCR is used, weather data must [039] be processed using World Meteorological Organization (WMO) headers.

#### Weather and NOTAM Products

The weather products [050] and NOTAM [051] products, including product sizes, issue times, formats, and retention periods must be as indicated in Appendix C.

#### Full Text Products

The DUAT Service must provide users with the option of receiving alphanumeric products in either:

- Normal transmission format (abbreviated) [052] or

- Expanded English text (unabbreviated) [053].

#### ICAO Weather Codes

The DUAT Service must implement the aeronautical meteorological codes as referenced in the Aviation Routine Weather Report (METAR) [054]; Aviation Selected Special Weather Report (SPECI) [055], Aerodrome Forecast (TAF) [056], and the Canadian Forecast Advisories (FAs) [830].  The ICAO code formats are published in ICAO Document 7910.

#### Surface Weather Observations

Throughout this specification, the term "hourly surface observation(s)" refers to METAR observation(s), which is recorded on the hour.  The term "special observation(s)" or "special(s)" refers to SPECI observation(s) which are recorded when special criteria are met or exceeded.  (Note:  See FAA Order 7900.5, Surface Weather Observing, for a complete description of current weather message formats).

#### Data Retention

The DUAT Service must retain in dynamic databases the latest version of any weather or NOTAM product, unless it has expired, exceeded its valid period, been canceled, or the retention time indicated in Appendix C has been exceeded [057].

#### Data Purge

The DUAT Service must purge from its dynamic database, within one hour, products that have:

- Expired, [060]

- Exceeded their valid period, [061]

- Exceeded their retention period, [062] or

- Been canceled [063].

#### Corrected or Amended Weather Products

When a weather product is received by the DUAT Service indicating that it is a Correction (COR) or Amendment (AMD) to a previously issued product, the COR [064] or AMD [065] product must be considered the latest version.  The retention period for COR or AMD products is based on the retention time of the original product.

#### 3.2.1.3.3.6  Reserved

#### 3.2.1.3.3.7  Routine Delay Weather Products

Weather products that are transmitted after their scheduled time may contain a Routine Delay (RTD) indicator.  When a weather product is received by the DUAT Service indicating that it is a RTD, it must [066] be retained in the database according to its data type, location/product identifier (ID), and date/time, just as any other incoming product.

#### Processing Requirements

All transactions must [932] be completed in a timely manner.  A transaction begins when a user successfully logs onto the DUAT Service and ends when the connection is terminated in accordance with the provisions of paragraph 3.2.1.5.1.6.  The functions included within one transaction are defined in paragraph 3.2.1.4.5.1.

#### Database Maintenance

#### 3.2.1.4.1.1	Alphanumeric Weather Data

The DUATS must receive [067], process [068], and maintain [069] a dynamic weather database using alphanumeric products provided by WMSCR or a comparable system or service.

#### 3.2.1.4.1.2	Reserved

#### 3.2.1.4.1.3  Static Flight Data

The DUAT Service must use the current versions (including posted changes) of the Government-Furnished Information (GFI) listed below for data maintenance editing and verification:

- Airman's Information Manual, [074]

- En Route Charts (High and Low), [075]

- National Airman Files, [076]

- Airport Facility Directory, (AFD) [077]

- Digital Aeronautical Chart Supplements, (DACS) [078]

- National Flight Data Digest (NFDD), [079]

- US Terminal Procedures (USTP), [080]

- World Aeronautical Charts (WACs), [081] and

- Static Flight Data (as described in Appendix A) [083].

Sources for GFI are identified in Section J7.

#### 3.2.1.4.1.4	User Directory Assistance

The DUAT Service must provide authorized users with on-line access to an Airport Facility Directory [820].  The SP must obtain FAA approval before providing additional information [821].

#### Weather Message Identification

The DUATS must identify all incoming messages and store them with the date [084] and time of receipt [085].

#### Weather Message Text Editing

The DUAT Service must [086] not edit or alter the content of weather and NOTAM messages, except header information.  Header information (e.g., data type, product ID, or date-time) may be altered to facilitate processing and storage.  Converting designated messages to expanded English text does not constitute an edit or alteration of the message.

#### Weather Message Duplication

If the DUAT Service receives a duplicate weather product from a Government approved weather source, the SP must [087] consider the product received last as the latest version.

#### 3.2.1.4.3  Weather Information Function

#### Weather Briefing Formats

The DUAT Service must provide users with weather briefings, as follows:

- Standard Weather Briefing, [088]

- Outlook Weather Briefing, [089] and

- Abbreviated Weather Briefing. [090]

The DUAT Service weather briefing types and their presentation formats are shown in Table 3.2.1.4.3.1-1.

Table 3.2.1.4.3.1-1: Weather Briefing Types

| Briefing Type | Format |
| --- | --- |
| Standard Weather Briefing | Route |
|  | Area |
| Abbreviated Weather Briefing | Route |
|  | Area |
| Outlook Weather Briefing | Route |
|  | Area |

NOTE:  Each briefing type consists of a low altitude briefing for flights below 18,000 feet MSL or a high altitude briefing for flights above 18,000 feet MSL.

#### Standard Weather Briefing

The DUAT Service must [091] provide users with a Standard Weather Briefing, as follows.

#### Input

For a Standard Weather Briefing, the DUAT Service must require the user to submit the following information:

- Aircraft identification; [092]

- Briefing format (route or area) (optional); [093]

- Estimated time of Departure; (ETD) [094]

- For route format only:

- Departure point, [095]

- Destination point, [096]

- Alternate destination(s) (optional), [097]

- Route of flight (optional), [098]

- * Route corridor width (nm) (optional), [099]

- * Winds aloft route corridor width (optional), [100]

- Flight altitude(s), [101]

- Estimated time en route (ETE); [102]

- For area format only:

- A center point for the search area (LOCID or latitude/longitude) [103] and

- A search area radius (optional); [104]

- Option for Air Traffic Control (ATC) delay and flow control advisories. [105].

NOTE: * If no value is entered, the default value identified in Appendix B must [106] be used.  Adaptable parameter values are contained in Appendix B.

#### Output

For a Standard Weather Briefing, the DUAT Service must label, segment, and output available weather products and NOTAM data to the user for either the identified route or area, as follows:

- Adverse weather products affecting the route corridor or area, [107]

- Latest surface observations for departure point, destination, and, if selected, alternate(s), [108]

- Latest terminal forecasts for departure point, destination, and alternate(s), [109]

- * En route weather -- surface observations along the route corridor [110]  (May provide En Route FTs),

- Pilot Reports (PIREPs) within the route corridor or area for the last 90 minutes, [111]

- Forecast winds and temperatures aloft, [112]

- Latest radar reports affecting the route corridor or area, [113]

- NOTAMs pertinent to the route corridor or area, [114] and

- **ATC delay and flow control advisories, if pertinent to the route corridor or area (user option). [115]

* Not required for high altitude briefings

** Provide as a user-selected option (see 3.2.1.4.4.30 for content)

#### Abbreviated Weather Briefing

The DUAT Service must [116] provide users with an Abbreviated Weather Briefing, as described in the following Subsections.

#### Input

For an Abbreviated Weather Briefing, the DUAT Service must require the user to submit the following:

- Aircraft identification, [117]

- Weather report type(s) desired for the identified locations, [118]

- *Up to 10 LOCIDs (optional), 119]

- *State identifier(s) (optional), [120]

- **Flight altitude, [121]

- ETD, [122]

- **ETE, [123]

- ***Route of flight, [761]

- ***Route corridor width, [762]

- ****Center point for search area (LOCID) or latitude/longitude, [763] and

- ****Search area radius (optional). [764]

NOTE:

*        Users may request products for 10 LOCIDs or opt to request state

collectives for those selected products.

**      Entry required only when a FD data type has been requested.

***    Entry required only when a route oriented briefing has been requested.

****  Entry required only when an area oriented briefing has been requested.

#### Output

For an Abbreviated Weather Briefing, the DUAT Service must [124] retrieve, label, segment, and output to the user all requested products (available in the database) in the order requested.

#### Outlook Weather Briefing

The DUAT Service must [125] provide the user with an Outlook Weather Briefing when the ETD is 6 or more hours from the briefing time.  The Outlook Weather Briefing is the same as the Standard Weather Briefing except as noted in sections 3.2.1.4.3.1.3.1 and 3.2.1.4.3.1.3.2.

#### Input

For an Outlook Weather Briefing, the DUAT Service must [126] require the user to enter the same information as the Standard Weather Briefing except for winds aloft route corridor width.

#### Output

For an Outlook Weather Briefing, the DUAT Service must label, segment, and output the same weather products as for a Standard Weather Briefing, except as follows:

(a)  Omit current weather conditions (surface observations, PIREPs, and radar reports), [127]

(b)  Omit forecast winds and temperatures aloft, [128]

(c)  Omit NOTAMs, [129] and

(d)  Omit ATC delay and flow control information. [130].

The DUAT Service must [131] provide the user the option to receive the omitted information (i.e., items a through d, above).

#### 3.2.1.4.3.2  Adverse Weather Products

#### Standard and Outlook Weather Briefing

If, for Standard Weather or Outlook Weather Briefings, adverse weather products (as defined in appendix C) exist which affect the route corridor or search area, the DUAT Service must [132] output all applicable adverse weather products, except as noted in the subsections below.

#### Tropical Advisories

When the user selects a Standard or Outlook Weather Briefing, and a Tropical Depression and Hurricane Advisory or an Atlantic/Pacific Ocean Tropical Cyclone Advisory affects the route, the DUAT Service must [133] display an alert message giving the user the opportunity to review or decline review of the report(s).

#### Reserved

#### Severe Weather Outlook

When the user selects a Standard or Outlook Weather Briefing, the DUAT Service must [134] address those portions of the Area Forecast that affect the user-specified route or area.

When the user selects a Standard or Outlook Weather Briefing and a Severe Weather Outlook affects the route corridor or search area, the DUAT Service must [765] either automatically output the product or give the user the opportunity to review or decline to review the product.

#### Abbreviated Weather Briefing

If, for an Abbreviated Weather Briefing, adverse weather products exist which affect the locations requested, the DUAT Service must [135] display an alert message giving the user the opportunity to review or decline to review these products.  The DUAT Service must [136] display the Abbreviated Weather Briefing alert message prior to providing any requested information.

#### 3.2.1.4.3.2.3  Area Forecast Output

When the user selects a Standard or an Abbreviated Weather Briefing, the DUAT Service must [137] display all sections of the Area Forecast when the user selects Area Forecast as a report type.

#### Trend Weather Products

The DUAT Service must [138] have the capability to produce a Trend Weather Product (TW) consisting of the current surface observation, the previous two hourly surface observations, and all subsequent SPECI observations or off-hour METAR observations for a weather reporting location.

#### Trend Weather Product Requests

In response to an Abbreviated Weather Briefing request, the DUAT Service must [139] output a TW for any requested valid weather reporting station’s LOCID.

#### Forecast Winds and Temperatures Aloft

The DUAT Service [140] must use either the Forecast Winds and Temperatures Aloft (FD) or the Gridded Winds and Temperatures Aloft Forecast (GF) to interpolate for flight level winds issued 4 times a day.  The DUAT Service must interpolate between forecast levels and output flight level data for the departure point [141], destination [142], and at least every 200nm along the route corridor [143].

#### Output Time Period

The DUAT Service must retrieve and output the data with the "Valid Time" [144] and "For Use" [145] period, based on the FD or GF winds and temperatures used for the interpolation.

#### Alternate Airport Weather

Any time an alternate airport(s) has been designated by the user, the DUAT Service must supply the user with alternate airport data, as follows:

- Any adverse weather products affecting the alternate(s) that have not already been provided [146]

- Current hourly surface observation(s) [147] and any subsequent SPECI or off-hour METAR observations [148]

- Terminal forecast(s) [149]

- NOTAMs [150].

#### Closest Reporting Location

If terminal weather is unavailable for the departure and/or destination, the DUAT Service must output corresponding products, as follows:

- Current hourly surface observation for the nearest location [151] and any subsequent SPECI or off-hour METAR observations [152]

- Terminal forecast for the nearest location, only if it is within 5 miles of the requested location [153].  If no terminal forecast is available, the DUAT Service must [154] output the latest FA which encompasses the area of the requested terminal forecast.

#### Collective Products

In response to a Weather Briefing request, the DUAT Service must allow the user to request state collectives of user-selected weather product types [155].

#### Weather Briefing Entry Carryover

The DUAT Service must [156] carry forward into the flight plan all weather briefing data related to the flight planning function.

#### Use of Previous Route

When a user has filed a flight plan(s) during the current transaction, the DUAT Service must provide the opportunity for using that route data [157] or route data from any of the users' own pre-stored flight plans [158] for obtaining a Route Weather Briefing.

#### 3.2.1.4.3.10  Reserved

#### Product Retrieval

#### Weather Product Search Area

The DUAT Service search area for weather product retrievals must be by a user-defined area (center point and radius)[187] or a route corridor [188].

#### Retrieval Processing

All weather and NOTAM data in Appendix C are classified according to a type of aerial coverage (point or area).  The DUAT Service must [189] retrieve a product when its affected area coincides with or infringes on the search area of interest.

#### NOTAMs

With any standard weather briefing, the DUAT Service must retrieve distant NOTAMs [190] and Flight Data Center (FDC) NOTAMs [191] associated with an affected facility by the affected facility identifier.  (Note: See FAA Order 7930.2 for terms of reference).

#### Non-associated Facilities

When an FDC NOTAM is requested and non-associated NOTAMs exist, the DUAT Service must [192] output a response to the user, stating:

"There are non-associated FDC NOTAMs current.  Do you want them?”  Or provide another FAA-approved message.

This response is to indicate to the user that FDC NOTAMs not associated with an affected facility identifier will not be presented unless the user specifically chooses to receive such information.

#### Reserved

#### 3.2.1.4.3.13   Graphic TFRs

Temporary Flight Restrictions (TFRs) are a critical part of the National Airspace System and providing a graphic display of these TFRs is an important aspect of a pilot’s flight planning.  These graphic displays provide for enhancement of all pilot weather briefings and flight planning.  To maintain the FAA’s highest level of safety for the NAS and flight planning, DUAT Service must provide graphic TFR displays. [767]

#### 3.2.1.4.3.14   Superseded Products

The DUAT Service must not output weather [193] or NOTAM [194] products to users for which later versions have been received.

#### 3.2.1.4.3.15  DUAT Service Interruptions

#### 3.2.1.4.3.15.1   Short-Term Weather Data Interruption

In the event of a short-term weather data interruption (one lasting less than 15 minutes), the DUAT Service must utilize the most recently received weather [195] and NOTAM [196] data.

#### 3.2.1.4.3.15.1.1    Short-Term Interruption Message

At the end of the first minute of the short-term interruption of incoming weather data, the DUAT Service must [197] output the following message:

“Weather/NOTAM data may not be current due to loss of incoming data at

[Zulu time] Z.   A recheck of data prior to departure may be warranted.”  Or provide another FAA-approved message.

The DUAT Service must output the short-term interruption message until the weather/NOTAM databases have been restored [198] or for up to 15 minutes after the onset of the interruption of service [199], whichever occurs first.

#### 3.2.1.4.3.15.1.2   Short-Term Interruption Resumption

The DUAT Service must develop and implement procedures to determine when the database has been fully updated with the data backlog from WMSCR [200] or other comparable system or service and the short-term interruption message withdrawn [201].

#### 3.2.1.4.3.15.2   Long-Term Weather Data Interruption

In the event of a long-term weather data interruption (one lasting 15 minutes or more), the DUAT Service must not provide weather [202] and NOTAM [203] data to users.

#### 3.2.1.4.3.15.2.1  Long-Term Interruption Message

When the interruption of incoming weather data reaches 15 minutes, the DUAT Service must [204] output the following message:

“No Weather/NOTAM data currently available due to loss of incoming data at [time] Z.  You may file a flight plan or access the system later for full service.”  Or provide another FAA-approved message.

#### 3.2.1.4.3.15.2.2  Long-Term Interruption Resumption

The DUAT Service must develop and implement procedures to determine when the database has been fully updated with the data backlog from WMSCR [205] or other comparable system or service, the interruption message withdrawn [206], and user services resumed [207].

#### 3.2.1.4.3.15.3   USNS-R Interruption

The US NOTAM Service Replacement (USNS-R) may issue a Circuit Notice (CIRNOT) advising of the unavailability of NOTAM information.  Following receipt of the CIRNOT, the DUAT Service must [208] display a message to users, as follows:

"NOTAM data may not be current due to a US NOTAM Service interruption.  A recheck of data prior to departure may be warranted.”  Or provide another FAA-approved message.

The DUAT Service must [209] output this message until it has been verified that the NOTAM database has been fully restored.

#### 3.2.1.4.3.15.4   DUAT Service System Failure

The DUAT SP must develop and implement procedures to ensure the weather [210] and NOTAM [211] databases are current and complete before user service is resumed.

#### 3.2.1.4.3.15.4.1   DUAT Data Base Rebuild

In the event the DUAT Service failure results in the loss of data already received, a partial or full database rebuild may be required.  The DUAT Service must [212] establish database rebuild procedures which result in full database restoration.

#### 3.2.1.4.3.15.4.2  DUAT System Failure Message

When the DUAT system returns to service, but is in the process of restoring the database, the following message, or another FAA approved message, must [213] be displayed to the users:  “No Weather/NOTAM data currently available due to system failure.  Full service is expected to resume at [time] Z.”

#### 3.2.1.4.3.16  Unavailable Weather Products

#### 3.2.1.4.3.16.1   Product Not in the Database

When a product request is valid, but not in the database, the DUAT Service must [214] output a response to the user stating “NO REPORT AVBL.”  Or provide another FAA-approved message.

#### 3.2.1.4.3.16.2   Invalid Product

When a product request cannot be provided because of invalid user input (i.e., invalid LOCID/product identifier and/or data type), the DUAT Service must [215] output a response to the user stating “NOT IN SYSTEM.”  Or provide another FAA-approved message.

#### 3.2.1.4.3.16.3  Invalid Format

When a product request cannot be provided because of an invalid format input, the DUAT Service must [216] output a response to the user stating "INVALID FORMAT.” Or provide another FAA-approved message.

#### 3.2.1.4.4  Flight Planning Function

The DUAT Service must provide users with the capability to:

- File flight plans, [217]

- Amend flight plans, [218]

- Store flight plans, [219]

- Cancel flight plans, [220] and

- Close flight plans (VFR only). [221].

#### Flight Planning Software Capabilities

The DUAT Service must provide authorized users the following Flight Planning software capabilities upon user entry of Flight Plan route, en route altitude and fuel consumption (gallons per hour):

For each leg of the flight plan route:

(1)  Magnetic heading (winds considered), [825]

(2)  True course, [826]

(3)  Leg length, [827]

(4) Leg estimated flight time, [828] and

(5) Fuel required. [829]

#### Stored Flight Plans

The DUAT Service must [222] permit the user to store flight plans.  Stored flight plans do not have to be complete and/or validated until they are filed.

The DUAT Service must permit:

(a)	Private pilots to store 10 flight plans [701] and

(b) Part 135 Operators to store at least 20 aircraft identifications [751], 20 pilots [752] and 100 routes. [753].

The DUAT Service must [703] have the capability to store at least 100,000 flight plans.

#### Message Formatting`

The DUAT Service must require that message formatting [223], coding [224], and text [225] for DUAT Service originated flight plans and related messages are in accordance with FAA Order 7110.10.

#### Flight Data Message Precedence

The DUAT Service must provide address fields [226] and message precedence [227] for all flight data messages, as required by FAA Order 7110.10.

#### Flight Plan Processing

The DUAT Service must accept and process only flight plans that are in accordance with the appropriate flight plan format [229], as specified in FAA Order 7110.10.

#### Domestic Flight Plan Processing

The DUAT Service must accept and process domestic IFR [230], and VFR [231] flight plans in compliance with all applicable orders and documents.

#### ICAO Flight Plan Processing

The DUAT Service must accept and process ICAO flight plans in which the departure point is a geographic point within the contiguous United States, Alaska, Hawaii, Puerto Rico and the US Virgin Islands. [233] and comply with all applicable orders and documents [234].  The DUAT Service must [235] validate ICAO flight plans to the last known fix in the route. FAA Order 7110.10, Chapter 7, International Operations, provides the procedures and guidance for filing ICAO flight plans.

A flight plan cannot be filed from an airport located in a country outside of the areas listed above unless the FAA has an agreement with that country that complies with all applicable ICAO annexes and standards.

#### Adverse Weather Conditions

If the user has not already received a weather briefing during the current transaction, the DUAT Service must [236] advise the user of adverse weather conditions applicable to the route of flight.  The DUAT Service must require the user to accept or decline review of the adverse weather conditions [237].

#### Acknowledgments

The DUAT Service must process and store acknowledgment messages from Air Route Traffic Control Centers (ARTCC) [238] and AFSS/FSS [239].

#### IFR Flight Plans

The DUAT Service must accept domestic IFR [240] and ICAO IFR [241] Flight Plans up to the Air Traffic Control Transmit Time (ATCTT) prior to departure, as indicated in Appendix B.

DUAT Service must provide General Aviation (GA) Pilots the capability to file an IFR ADIZ Flight plan. [768]

#### IFR Parameter Time

When a domestic IFR [242] or ICAO IFR [243] flight plan is to be forwarded to an ARTCC, the DUAT Service must delay transmission of the flight plan until the ATCTT prior to the proposed departure time, as indicated in Appendix B.

#### Domestic and ICAO VFR Flight Plans

The DUAT Service must accept domestic [244] and ICAO VFR [245] flight plans up to the Flight Service Station Transmit Time (FSST) parameter time, as indicated in Appendix B.

#### Domestic and ICAO VFR Parameter Time

When a domestic [246] or ICAO [247] VFR flight plan is to be forwarded to a AFSS/FSS, the DUAT Service must delay transmission until the FSST parameter time prior to the proposed departure time, as indicated in Appendix B.

#### Alaska Flight Plans

The DUAT Service must [248] provide the user with the ability to file VFR flight plans in Alaska with a maximum of two weeks en route time.  Round-robin flight plans are acceptable.

#### File Flight Plan with ARTCC

The DUAT Service must prepare domestic IFR [249] or ICAO IFR [250] flight plans in accordance with FAA Order 7110.10.  The DUAT Service must file the IFR [251] and ICAO [252] flight plans with the departure ARTCC.

#### Multiple Flight Plans

The DUAT Service must [253] accept multiple flight plans per aircraft identification.

#### Dispatcher Flight Plans

The DUAT Service must allow multiple flight plans to be filed [254] and stored [255] from one source (such as a corporate dispatcher or an airline) only after obtaining the identification of the dispatcher(s) involved and the flight identification(s).

#### Formatted Flight Plans

The DUAT Service must:

- Format flight plans in accordance with FAA Order 7110.10. [259]

- Transmit them to the appropriate ARTCC [260] or AFSS/FSS [261], at a parameter transmit time before the proposed departure time.

#### Data Transmission

The DUAT Service must [262] transmit flight plan data in accordance with FAA Order 7110.10.

#### Flight Plan Storage

#### IFR Flight Plan Storage

The DUAT Service must store domestic IFR [263] and ICAO IFR [264] flight plans from time of receipt until an ATCTT parameter time prior to the proposed departure time, as indicated in Appendix B.

#### VFR Flight Plan Storage

The DUAT Service must store domestic [265] and ICAO VFR [266] flight plans from time of receipt until a FSST parameter time prior to the proposed departure time, as indicated in Appendix B.

#### Time Modifications

The DUAT Service must [267] have the capability to modify the ATCTT parameter time as capacity warrants.

#### Duplicate Flight Plans

The DUAT Service must not accept [268] or transmit [269] duplicate flight plans, except as identified in subsection 3.2.1.4.4.16.

#### Flight Plan Acknowledgments

#### 3.2.1.4.4.16.1  IFR Acknowledgment

When a valid acknowledgment response has not been received from the addressed ARTCC for a domestic IFR flight plan within 5 minutes of its transmission, the DUAT Service must [270] immediately re-transmit the flight plan to the ARTCC.

If an acknowledgment is not received for the re-transmitted domestic flight plan, the DUAT Service must [272] deliver the flight plan, via telephone, to the ARTCC Flight Data Position within 10 minutes after the time the initial flight plan was transmitted.

#### 3.2.1.4.4.16.2  VFR Acknowledgment

When a valid acknowledgment has not been received from the addressed AFSS/FSS for a domestic [276] flight plan within 15 minutes of its transmission, the DUAT Service must immediately re-transmit the flight plan to the AFSS/FSS.

If an acknowledgment is not received for the re-transmitted domestic [278] flight plan, the DUAT Service must deliver the flight plan, via telephone, to the AFSS/FSS within 30 minutes after the time the initial flight plan was transmitted.

#### Error/Reject Messages

#### Error Message Procedures

In the event an error message is received from the addressed ARTCC, the DUAT Service must observe the following procedures:

- Immediately transmit a cancellation message (CXX) to delete the erroneous flight plan from the ARTCC database, [280]

- Correct the flight plan, as indicated within the ARTCC error message, and re-transmit the revised flight plan to the ARTCC, [281]

- If either the route or altitude must be altered, enter "FRC" (Full Route Clearance) as the first element in the Remarks Section of the revised flight plan, [282] and

- If, after transmitting the revised flight plan, a second error message is received, transmit a second cancellation message and call the ARTCC to input the flight plan manually. [283].

#### Reject Message Procedures

In the event a reject message is received from the addressed ARTCC, the DUAT Service must observe the following procedures:

- Attempt to correct the flight plan, as indicated by the reject message, and re-transmit the revised flight plan to the ARTCC; [284]

- If, after transmitting the revised flight plan, a second reject message is received, call the ARTCC to input the flight plan manually; [285]

- If either the route (including inserting a lat/long into the route of flight for Center acceptance) or altitude must be altered, enter “FRC” as the first element in the Remarks Section of the revised flight plan; [286] and

- If the reject message is identified as being an exact duplicate, the message is not to be re-transmitted. [287]

#### Flight Plan Filing

The DUAT Service must [288] allow a user to submit a domestic flight plan any time from 30 minutes to 24 hours before the proposed departure time and an ICAO flight plan any time from one hour to 24 hours before the proposed departure time.

Flight plans with waypoints must [040] be filed by the SP in accordance with FAA Order 7110.10.  If an error message is received from the addressed ARTCC and a waypoint needs to be altered the SP must [058] enter “FRC” (Full Route Clearance) as the first element in the remarks section of the revised flight plan.  The SP must [059] make only those changes required for computer acceptance.

#### Lifeguard Flights

The DUAT Service must [289] accept Lifeguard and US Coast Guard flight plans, as designated in FAA Order 7110.10, up to 10 minutes before the proposed departure time.

#### Flight Plan Input

The DUAT Service must [290] require the user to enter flight plan data required by the applicable FAA flight plan form.

#### Domestic Flight Plan Acceptance

The DUAT Service must [291] not accept domestic flight plans unless all the required flight plan data blocks indicated on FAA Flight Plan Form 7233-1 contain valid entries in accordance with FAA Order 7110.10.

#### ICAO Flight Plan Acceptance

ICAO flight plans must [292] not be accepted by the DUAT Service unless all the required flight plan data blocks indicated on FAA Flight Plan Form 7233-4 contain valid entries in accordance with FAA Order 7110.10.

#### Incorrect Entries

When the user makes an incorrect entry, the DUAT Service must [293] identify the error and give the user the opportunity to correct the entry.

#### Format Checking

The DUAT Service must perform format checks on the user entry [294] and, upon format verification, initiate flight plan filing procedures [295].

#### Latitude-Longitude Entry

If a latitude-longitude is entered on the flight plan for departure [296] or destination [297], the DUAT Service must ensure the location name is carried in the remarks section.

#### Washington, DC Metropolitan Area Flight Restricted Zone (DC FRZ)

The DUAT Service must [071] reject to the user all flight plans calling for entry into the DC FRZ unless the user is a DOD, Law Enforcement, or wavered Lifeguard/Aeromedical flight or has filed an IFR or DC FRZ flight plan with a discrete code assigned by an ATC facility.

#### Flight Plan Display

When all required entries have been completed and contain acceptable data, the DUAT Service must [298] output a complete flight plan to the user.

#### Flight Plan Modification/Filing

When a flight plan is output to the user, the DUAT Service must allow the user to file the flight plan [299] or to modify any of the data blocks before filing the flight plan [300].

#### Weather Briefing Update

When the user modifies any of the data blocks in the flight plan, the DUAT Service must [301] prompt the user for the opportunity to receive a new weather briefing.

#### Re-output Modified Flight Plan

When the user modifies any of the data blocks, the DUAT Service must [303] re-output the entire flight plan to reflect the modification.

#### Continuation of Changes

The DUAT Service must permit the user to modify the flight plan until the user stores the flight plan [304], files the flight plan [305], or selects another DUAT Service function [306].

#### Completion Message

When the flight plan has been validated and accepted, the DUAT Service must [307] output a message to the user indicating the validation and acceptance.

#### Reserved

#### Route Definition

The DUAT Service must allow the user to enter flight plan routes according to the following route elements:

- LOCIDs; [308]

- Fixed Radial Distances; [309]

- Latitudes and longitudes, [310]

- Control, Victor, Jet, Colored Airways, Area Navigation, Bahamas Routes and Atlantic or any other approved FAA route elements; [311]

- Standard Instrument Departure; [312]

- Standard Terminal Arrival Route; [313]

- Navigation aids; [315]

- LF/MF Airways and Oceanic Low/High frequency routes; [316]

- Tower En Route Control (TEC) routes; [317]

- Waypoints; and

- Any valid combination of the above. [318]

Note:    If the user chooses to use a Standard Instrument Departure (SID) or Standard Terminal Arrival Route (STAR) in an ARTCC area that does not accept SIDs or STARs, the user will enter them in the remark area only.

#### Valid Elements and Fixes

The DUAT Service must [319] validate all domestic route elements against the Static Flight Data, as provided in Appendix A.  There is no requirement to validate a VFR route of flight.

#### Route Contiguous Legs

For IFR flight plans, the DUAT Service must [320] require that the legs of an IFR route be contiguous.

#### Previously Entered Data

When the user has previously entered an acceptable route to obtain a weather briefing, the DUAT Service must [321] allow the user to use this route for the flight plan without reentering the data.

#### Preferred Routes

The DUAT Service must maintain files containing preferred IFR low [322] and high [323] altitude, and Tower En Route Control (TEC) routes [324].

#### Preferred Route Selection

When the user provides a departure point, proposed departure time, aircraft type, altitude, and destination, the DUAT Service must provide the user with the opportunity to select from the preferred routes [326] and automatically insert the route data into the route of flight [327].  	Preferred route processing must be applied when an IFR flight plan is filed [328] or amended [329].

#### Flight Plan Amendments/Cancellations

The DUAT Service must allow the user to amend [330] or cancel [331] flight plans, which were previously accepted, but not transmitted to the appropriate facility.

#### Authorization

The DUAT Service must permit the user to amend [332] or cancel [333] flight plans only with the same access code used to originally file it.

#### Flight Plan Retrieval

The DUAT Service must allow the user to select a flight plan(s) to be amended [334] or canceled [335] by retrieving and displaying all stored flight plans on file for the access code/aircraft identification entered.

#### Flight Plan Amendments

The DUAT Service must [336] allow the user to amend a flight plan at any time prior to transmission of the flight plan to the appropriate FAA facility (including a destination change or a lat/long insertion.  When this occurs, the route of flight will be re-verified for Center acceptance.

#### Flight Plan Time Limits

When the user attempts to amend a flight plan after transmission to the appropriate FAA facility, the DUAT Service must [337] advise the user to contact an AFSS/FSS.

#### Flight Plan Entry Carryover

The DUAT Service must [338] carry forward into the weather briefing all flight plan data related to the weather briefing function.

#### Acceptance Messages

The DUAT Service must [339] output a message to the user indicating the amended flight plan has been validated (error and format checked) and accepted.

#### 3.2.1.4.4.28  Cancel Flight Plans

#### Flight Plan Retention

When the user cancels a flight plan proposal, the DUAT Service must [340] retain the flight plan data with the transaction data for event reconstruction.

#### Time for Cancellation

The DUAT Service must [341] provide the user with the ability to cancel a flight plan at any time between the flight plan acceptance and transmission to the appropriate facility.

#### Message After Cancellation

When the user identifies the flight plan to be canceled, the DUAT Service must [342] output a confirmation message to the user indicating that the flight plan has been canceled.

#### Notification of Transmission

If a request for cancellation is made and the flight plan has already been transmitted, the DUAT Service must [343] advise the user to contact an AFSS/FSS.

#### No Flight Plan Message

When no flight plan proposals have been received for the entered access code and aircraft identification, the DUAT Service must [344] output a FAA-approved message indicating that no flight plan exists for the aircraft identification entered.

#### VFR Flight Plan Closure

The DUAT Service must accept and transmit to the tie-in AFSS/FSS, domestic [345] and ICAO VFR [346] flight plan closure messages when the destination is in the contiguous U.S., Alaska, Hawaii, Puerto Rico, or the U. S. Virgin Islands.

#### Flight Plan Closure Acceptance

The DUAT Service must not accept domestic [347] and ICAO VFR [348] flight plan closures without the minimum required entries to process the closure.

#### Required Entries

To accept domestic and ICAO VFR closures, the DUAT Service must require, as a minimum, the following entries:

- Aircraft Identification, [349]

- Aircraft Type, [350]

- Departure Point, [351]

- Flight Planned Destination Point, [352]

- Pilot Remarks, e.g., location of aircraft if other than planned destination (optional entry). [353].

#### Closure Message

The DUAT Service must generate and transmit a domestic [354] or ICAO VFR [355] closure message to the destination tie-in FSS, in accordance with FAA Order 7110.10, within 2 minutes of the pilot's notification of closure.

#### Receipt of Closure Message

When the user inputs a domestic [356] or ICAO VFR [357] flight plan closure, the DUAT Service must output a confirmation message to the user, indicating that the closure message has been sent.

#### Acknowledgment

When an acknowledgment is not received for any domestic [358] flight plan closure within 10 minutes, the DUAT Service must immediately deliver the flight plan closure via telephone to the flight planned destination AFSS/FSS.

#### Traffic Management Function

The DUAT Service must allow the user to view, in full text, the traffic management information concerning air traffic delays (ATCSCC messages) [360] and reroutes [361].  The DUAT Service must [362] strip the message information following the string “FSx.//”, where “x” is any alphabetic character.

NOTE:  References to persons-to-call and telephone numbers in ATCSCC messages are removed before the messages are made available to the general user population.  This information follows the character string “FSx.//”, where “x” represents any alphabetic character, and appears at the end of an ATCSCC message.

#### Encode/Decode Functions

Encoding involves the conversion from a location name to the assigned LOCID.  Decode involves the conversion from a LOCID to a location name.

The DUAT Service must provide encode [363] and decode [364] functions for domestic locations in accordance with the information contained in FAA Order 7350.7.

The DUAT Service must provide encode [365] and decode [366] functions for ICAO locations in accordance with the information contained in ICAO 7910.

Note: Some Canadian and Mexican locations are also listed in FAA Order 7350.7.

#### Domestic Location Information

When accomplishing domestic decode, the DUAT Service must [367] provide the user, as a minimum, the associated location information contained in FAA Order 7350.7 (i.e., associated ARTCC and tie-in AFSS/FSS).

#### ICAO Area of Responsibility

The DUAT Service must be responsible for encode and decode for the following ICAO areas:

- Canada, [368]

- Mexico, [369]

- Bahamas, [370]

- Puerto Rico, [371]

- Haiti, [372]

- Dominican Republic, [373]

- Virgin Islands, [374] and the

- Cayman Islands. [375]

#### Escape to Encode/Decode Function

The DUAT Service must allow the user the capability to escape from any DUAT Service function and go to Encode/Decode Function [376] and then return to the original function [377].

#### Data Recording and Retention

#### Event Recording and Reconstruction

The DUAT Service must provide Event Recording [378] and Reconstruction [379] for all user transactions to aid in aircraft accident/incident investigation.

#### Transaction Recording

The DUAT Service must record each user transaction in its entirety, to include:

- All inputs. [380]

- All outputs, [381] and

- All messages related to the transaction. [382]

#### Event Reconstruction

The DUAT Service must have the capability to retrieve data to recreate a specific recorded user transaction in its entirety, to include:

- All inputs, [383]

- All outputs except weather graphics, [384] and

- All messages related to the transaction. [385]

Although weather graphic products are not required for the reconstruction data, the DUAT Service must [704] identify each specific weather graphic product provided to the user.

#### Event Retrieval Key

The DUAT Service must [386] use aircraft identification as the primary key to retrieve the event reconstruction data.

#### Event Retrieval Time Period

The DUAT Service must have the capability to retrieve event data for 15 calendar days plus partial data for the current day [387] or for a specified start/stop time interval within the period [388].

#### Transaction Data Retention

The DUAT Service must retain all recorded user transaction data, as follows:

- Alaskan flight plans, 15 calendar days plus partial data for the current day after proposed flight closure [389]

- All other flight plans, 15 calendar days plus partial data for the current day after the transaction date and time [390].

#### Incoming Weather and NOTAM Data

The DUAT Service must provide for the recording, retention, and retrieval of all received:

- Alphanumeric weather products [391]

- NOTAMs [393].

#### Weather and NOTAM Data Recording

The DUAT Service must time-stamp all incoming weather [394] and NOTAM [395] data.

#### Weather and NOTAM Data Retention

The DUAT Service must retain all incoming alphanumeric weather products [396] and NOTAM data [397] for 15 calendar days plus partial data for the current day from the time of receipt.

#### Data Retrieval

The DUAT Service must have the capability to retrieve weather and NOTAM data from the record retention period by:

- LOCID, [398]

- Data type, [399]

- Product identification, [400]

- Date-time, [401]

- Start/stop time interval, [402] or

- Any combination of the above. [403]

#### Time-Stamp Display

The DUAT Service must [404] display the received time stamp on all weather [405] and NOTAM [406] data retrieved from the 15 calendar days plus partial data for the current day retention file.

#### Event Reconstruction Requests

The DUAT Service must [407] make event reconstruction data available in response to Q signal messages requests, any general Service B message request, and  verbal requests, when followed by written or FAX requests on letterheads, received from FAA intra-agency offices (e.g., FAA flight Service stations, FAA air traffic control facilities, etc.).  Other agencies requiring event reconstruction support from the DUAT Service will submit a written request or FAX (with letterhead) to the DUAT Service Contracting Officer (CO):

Federal Aviation Administration

ATTN: DUAT Contracting Officer, AJA-48

800 Independence Avenue, SW

Washington, DC 20591

Phone: (202) 267-3610

Fax:	(202) 267-5412

#### Request Response Time

For Event Reconstruction, the DUAT Service must [414] respond to the requesting organization or agency within 48 hours of receipt of the request.

#### Search and Rescue Requests (SAR)

The DUAT Service must perform a search of the event reconstruction data to satisfy the following SAR requests:

- Data Request on Aircraft (QALQ) [415] or ICAO equivalent (DETRESFA), [1046]

- Information Request (INREQ) [416] or ICAO equivalent (INCERFA), [417]

- Alert Notice (ALNOT) [418] or ICAO equivalent (ALERFA), [419] and

- A request from an authorized agency [420] as identified in subsection 3.2.1.4.4.33.3.

#### SAR Response Time

The DUAT Service must respond to a SAR requester within 15 minutes after receipt of the request, either automatically [421] or manually (telephone) [422], as specified in FAA Order 7110.10.

#### SAR Response Order

If there are multiple SAR requests, the DUAT Service must [423] respond to each SAR request message in the order in which they were received.

#### Data Search

The DUAT Service must [424] begin the SAR request data search with the most recent data and continue back through the previous 24 hours unless the SAR request specifies a start/stop time interval.

#### Continuation of Search

When a SAR request is active, the DUAT Service must [425] continue to monitor current in-coming transactions for the affected aircraft identification.

Note:  If the SAR request is a start/stop time type request whose time interval negates the need for on-going monitoring, a continuation search is not required.

#### Data Retrieval

The DUAT Service must [426] search for recorded transactions by the aircraft identification submitted in the SAR request [427] and, if appropriate, the start/stop time interval [428].

#### Response Data

The DUAT Service must include the following as SAR response data for the affected aircraft identification:

- All inputs, [429]

- All outputs, [430] and

- All messages related to the transaction(s). [431]

In responding to a SAR request, the DUAT Service must [432] not include the actual weather and NOTAM data provided to the user.

#### No Data Found in Search

The DUAT Service must immediately advise the requesting facility or agency when:

- No transaction data were found to satisfy the SAR request for the 24-hour period [433], or

- No transaction data were found in the SAR specified start/stop time interval [434].

#### DUAT Service Access

DUAT Service Access is defined as the probability that any attempt to access the DUAT Service made by an authorized user will result in a connection providing reliable bi-directional data transfer.  DUAT Service Access must [435] be 95 percent or greater.

#### Transaction Provisions

The DUAT Service must allow multiple functions within a transaction, including receiving weather information and graphics, filing multiple flight plans, etc., during the transaction time period [437].

#### Time Recording Accuracy

The DUAT Service must [438] record the times of transaction activities in at least tenths of a minute increment.

#### User Time Warnings

The DUAT Service must [439] advise the user when the last 2 minutes of the transaction has been reached.

#### Termination

#### Transaction Termination

The DUAT Service must [440] allow the user to terminate the transaction at any time.

#### Time-out Termination

The DUAT Service must [441] terminate the transaction if there is no user input for a total of three minutes from the user's last keyboard/mouse entry.

#### Time-out

The DUAT Service must [442] prompt the user for entry if there has been no keyboard/mouse activity for two minutes.

### 3.2.1.4.5.2.2.2   Reserved

#### 3.2.1.4.5.2.2.3  Termination Disconnect

The DUAT Service must disconnect the user from the DUAT Service upon the completion of a transaction [443].

#### Transaction Number

The DUAT Service must [444] assign and display to the user a unique transaction number for each transaction.

#### Sequence Assignment

The DUAT Service must assign transaction numbers sequentially, on a daily basis, beginning at 0000Z for the interactive DUAT Service [445].

#### Storage

The DUAT Service must [447] store the transaction number with the transaction for event recording and reconstruction.

#### User Information

#### FAA Information

The DUAT Service must provide a FAA Information Display [448] at the beginning of every transaction for the display of FAA messages and announcements.  The DUAT Service must allow the user the opportunity to access the FAA Information Display [449] or to proceed to the next desired function [450].

#### Input Error Detection

Whenever a user-input error is detected, the DUAT Service must [460] output a FAA approved message to the user identifying that error.

#### Reentering Data

When a user input error has been identified, the DUAT Service must [461] give the user an opportunity to reenter data correctly.

#### Date and Time Display

The DUAT Service must display the date and current Coordinated Universal Time Code (UTC) to the user at the beginning [462] and end [463] of each transaction.

#### Help Function

The DUAT Service must [464] provide an on-line help function to define and explain responses to DUAT Service user entries.

#### Help Function Field Entries

DUAT Service help messages must reflect the specified field entries [465], data types [466], and the required format [467].

#### Access to Help Function

The DUAT Service must [468] provide access to the help function any time the DUAT Service requires input from the user.

#### Expanded Help Function

In addition to assistance on individual prompts, the DUAT Service must provide an on-line, expanded help function that provides at least the following information:

- A detailed description of the DUAT Service from a user's viewpoint; [469]

- Instructions on how to use the DUAT Service, including examples; [470]

- A description of, and instructions on, the use of the control functions available to the user; [471] and

- A complete description of all command syntax and meanings, error messages and meanings, product display formats, and detailed help data. [472]

#### 3.2.1.4.7.4.  ICAO Help Function

The DUAT Service must [473] provide an ICAO help function that describes and provides examples of ICAO data to be entered for each field of the flight plan.

#### ICAO Help Function Entry

The DUAT Service must [474] allow entry to the ICAO help function from any ICAO flight plan function.

#### DUAT Service Help Line

The DUAT Service must [475] provide direct assistance to users via toll-free communications circuits.  The DUAT Service must [1040] provide direct assistance to users using an Internet interface.  The DUAT Service Help Line must [476] operate 24 hours a day, 7 days a week

#### Interface Requirements

#### Reserved

#### Reserved

#### Reserved

#### Reserved

#### Interface with NAS Systems

The SP must interface with the following National Airspace System (NAS) systems:

- National Airspace Data Interchange Network (NADIN) MSN Rehost (NMR) [1500];

- Weather Message Switching Center Replacement (WMSCR), if not using a comparable system or service; [1501];

- Air Traffic Control (ATC) Host Computer or its replacement, En Route Automation Modernization (ERAM); [1502];

- Air Traffic Control System Command Center (ATCSCC) [1503];

- Legacy AFSS/FSS System Interfaces  (i.e., OASIS and AISR) [1504];

- Flight Services 21 (FS-21)) [1505]; and

- Government communications circuits [1506].

#### Reserved

#### Atomatic Call Detection

The DUAT Service must provide automatic-answering [485] and automatic-baud detection and adjustment features [486].

#### Call-Termination

The DUAT Service must terminate connection:

- When originated by the user, [487]

- When there has been no user keyboard entry for 3 minutes, [488] or

- When the transaction is complete. [489]

#### DUAT TCP/IP Interfaces

The DUAT Service must [491] use IP as an intermediate pathway between the DUAT Service and other NAS and non-NAS systems.  The interface must [493] comply with NADIN TCP/IP services utilizing the Common Message Handling Protocol (CMHP) Interface Control Document (ICD), currently in draft and, if WMSCR is used, the interface must [492] comply with the Weather Message Switching Center Replacement (WMSCR) TCP/IP Services utilizing the Common Message Handling Protocol (CMHP) ICD, currently in draft.

#### NAS Messages

The DUAT Service must:

- Establish and maintain the electronic flight plan messages for data transmission to the NAS [496] and

- Receive and process rejected flight plan data messages from the NAS [497].

#### Originator's Address

Messages originated by the DUAT Service must [498] contain the originator's unique address indicator which will be assigned by the FAA.

#### Data Exchanges

Data exchanges between the DUAT Service and the FAA facilities must comply with the following FAA Publications:

- NAS-MD-310, [499]

- NAS-MD-311, [500]

- NAS-MD-312, [501]

- NAS-MD-315, [502]

- NAS-MD-316, [503] and

- FAA Order 7110.10. [504]

#### Performance Requirements

The DUAT Service must meet the performance requirements in Tables 3.2.1.6-1 and 3.2.1.6-2 (Requirements 505 through 523).

#### Simultaneous Users

The DUAT Service must [524] be capable of initially supporting at least 96 simultaneous users while meeting all functional and performance requirements of the specification.

#### Time Source Synchronization

The DUAT Service must [525] maintain the time reference synchronized to within one second of UTC, based on a FAA-approved time source.

Table 3.2.1.6-1: Processing Performance Requirements

| Item | Requirement | Mean | 99th Percentile | Maximum |
| --- | --- | --- | --- | --- |
| 1 | Connection establishment time: From connection until display of initial log-on screen | 3.0 [505] | 5.0 [506] | 10.0 [507] |
| 2 | Complete Flight Plan Route Validation | 2.0 [508] | 5.0 [509] | 10.0 [510] |
| 3 | Respond to Data Request | 2.2 [511] | 3.9 [512] | 8.3 [513] |
| 4 | Error Message Output | 2.0 [514] | 7.2 [515] | 8.3 [516] |
| 5 | Flight Plan Processing | 2.0 [517] | 5.0 [518] | 7.2 [519] |

Note:  All values are in seconds and a normal distribution is assumed.

Table 3.2.1.6-2: Data Performance Requirements

| Item | Requirement | Maximum |
| --- | --- | --- |
| 1 | Terminal, area, upper-air forecasts, and forecast amendments | 30 [520] |
| 2 | Surface Weather observations, PIREPs and radar reports (including special/urgent reports) | 15 [521] |
| 3 | Weather warnings and advisories | 15 [522] |
| 4 | NOTAMs | 30 [523] |

Note:  Maximum time is in seconds and is computed from time of data receipt until the product has been processed, stored, and is ready for use.  Product sizes are provided in Appendix C.

#### Flight Plan Error Rate

The DUAT Service error rate for flight plan messages filed with the ARTCC must [526] not exceed one (1) percent on a weekly basis.

Flight plan error rate must [527] be computed as the number of flight plan errors (a flight plan error message may identify more than a single error) divided by the number of flight plan messages filed, expressed as a percentage.

A flight plan reject message must [528] be counted as an error unless the reason for reject was for the flight plan being a duplicate transmission.

Other errors, which are determined by the FAA not to be the fault of the DUAT Service, will be excluded from the error rate computation.

#### 3.2.1.6.4  Qualified Internet Communications Provider (QICP) Requirement

The SP must achieve and maintain status as a QICP [1507].  As such, the SP must install and use Secure Socket Layer (SSL) encryption for CFR Part 121 and 135 operators to fully comply with requirements outlined in Advisory Circular AC 00-62, dated 11/01/02. [1508]

After the SP achieves QICP status, the SP must display a warning label on its Internet site. [1509]  The following language is recommended for the label:  This Qualified Internet Communication Provider’s (QICP) servers and communication interfaces are approved by the FAA as secure, reliable, and accessible in accordance with AC 00-62.  1) This QICP does not ensure the quality and currency of the information transmitted to you.  2) You the user, assumes the entire risk related to the information and its use.

#### 3.2.2     Reserved

### System Quality Factors

#### Reliability

The DUAT Service must [530] plan and implement reliability procedures to satisfy the performance and operational requirements of this specification.

#### Maintainability

The DUAT Service must [531] plan and implement maintainability procedures to satisfy the performance and operational requirements of this specification.

#### Availability

The DUAT Service must [532] maintain an operational availability (Ao) of 99 percent in any 30-day period.  For the purposes of availability calculations, down time is defined as anytime DUAT Service is unavailable to users within the mean times established in table 3.2.1.6-1.  Events such as natural disasters and Government communications circuits failures must [073] be included in the Ao calculations but these will not be counted against the SP’s service requirement.

DUAT Service availability must [536] be computed as:

Ao = (total time – total down time / total time) x 100

### System Flexibility and Growth

The DUAT Service must [537] be an open system capable of incorporating new products or other capabilities as they become available.

#### DUAT Service User Growth

The DUAT Service must [538] be able to accommodate a 5 percent annual growth in the number of transactions while still satisfying all functional and performance requirements of this specification.

### 3.3       Reserved

### Human Engineering

The user's personal computer or terminal must [542] provide the human interface to the DUAT Service.  The human interface is defined to be all display and data/command entry devices with which the user accesses or uses the DUAT Service.

#### Human Factors

Human factors requirements for error management/data protection must [543] comply with MIL-STD-1472, paragraph titled Error Management/Data Protection, except where superseded or extended by a requirement in this specification.

#### Command Language

The DUAT Service must [544] provide a data entry/command format for users to input data.

#### User Feedback

The DUAT Service must [545] provide feedback to all user data and command entry actions, with message output subject to FAA approval.

#### Feedback Message

The DUAT Service must provide a plain language text message or other distinct indication to confirm a requested system action [546], or an indication that the action was not performed [547].

#### Feedback Time

When any user request takes more than 3 seconds to complete, the DUAT Service must [548] provide a message/icon indicating that the system is working on the user's request.

#### Error Messages

The DUAT Service must generate system error messages [549] and user input error messages [550] written in plain language text.  The messages should aid the user as much as possible without reference to a FAA-approved manual.

#### Command Response Message

The DUAT Service must [551] respond to all fulfilled commands with an acknowledgment indicating successful completion.

#### Command Error Message

The DUAT Service must respond to all unfulfilled commands with messages identifying user input or syntax errors in these commands [552], and system errors detected in the performance of these commands [553].

### through 3.3.9	Reserved

#### 3.3.9.1	General Security Requirements

#### Physical Security

The DUAT Service must [554] provide Physical Security as defined in FAA Order 1600.69B.

#### Telecommunications and Information Security

The DUAT Service must provide Telecommunication and Information Security as defined in Information Systems Security Program; FAA Order 1370.82A, Chapter 3, Section 12 [555].

#### User Passwords

The DUAT Service must [557] protect user passwords in the database as defined in the FAA Information Systems Security Program; FAA Order 1370.82A.

#### Access Levels

The DUAT Service must provide the following three levels of access:

- Weather Briefing and Flight Planning, [558]

- Authorized Users Database Management, [559] and

- FAA Information Display. [560]

#### Weather Briefing/Flight Planning Access

The DUAT Service must restrict access to the Weather Briefing [561] and Flight Planning [562] Functions to persons listed in the Authorized Users Database or other FAA-authorized users.

#### Authorized Users Database Access

The DUAT Service must allow only FAA-authorized personnel to access [563] and update [564] the Authorized Users Database.

#### User Information Display Area Access

The DUAT Service must [565] allow only FAA-authorized personnel to access and update the FAA Information Display.

#### Reserved

#### Access Restrictions

The DUAT Service must [566] prevent unauthorized access to the DUAT Service.

#### Initial Access Validation

On initial use, DUAT Service must require the user to enter his/her last name [567] and his/her pilot certificate number [568] (if applicable) for validation with the Authorized Users Database.

#### Access Non-Validation

When the user-entered access data are not contained in the Authorized Users Database, the DUAT Service must [569] display a message to the user indicating that an access code cannot be issued because the DUAT Service was unable to validate the name and certification number (if applicable).

#### New DUAT User Access

If a new user is not listed in the Authorized Users Database, the DUAT Service must [570], upon receipt of a copy of the user’s Pilot Certificate or Student Medical Certificate, provide access to the DUAT Service.  Fax copies are acceptable.

#### Documentation Retention

The DUAT Service must [571] retain the copies of the new user’s Pilot or Medical Certificates until the user’s name appears in the updated Authorized Users Database.

#### Access Code and Password Assignment

Once a first time user has been verified, the DUAT Service must provide the user with an access code [572] and require the user to input a password [573].

#### Access Codes

The DUAT Service must [574] assign a unique access code to each user.

#### Access Security

To maintain security, the DUAT Service must [575] obscure the access code and password from the user terminal.

#### Password

The DUAT Service must allow the user to initially select [576] and change [577] his/her password at any time.

#### Retention for Future Use

Once the password is verified by the user and accepted, the DUAT Service must [578] display a message suggesting retention of the access code and password for future use.

#### Log-on

Upon each user's subsequent log-on, the DUAT Service must [579] authenticate the user's identity by requiring the entry of a valid access code and password.

#### Log-on Denial

After three attempts, DUAT Service must deny entry when user enters an invalid access code [580] or password [581].

.

#### Log-on Denial Remarks

In the event of an unsuccessful log-on, the DUAT Service must [582] display a message to the user indicating a log-on denial and a request that the user contact the DUAT Service Help Line at a specified telephone number.

#### Record of Log-on Attempts

The DUAT Service must [583] record both successful and unsuccessful log-on attempts.

#### 3.3.9.8	Scope of the Information Systems Security Program

The DUAT Service must [1021] provide the full scope of security as defined in the FAA Order 1370.82A, Chapter 1, Section 6 [1022] and Chapter 1, Section 4.  The DUAT Services must [1028] provide all the FAA ISS implementation directive guidance as defined in FAA Order 1370.82A, Section 7, a, b, and c.

#### 3.3.9.8.1  Security Implementation

The DUAT Service must [1033] implement all aspects of the FAA Order 1370.82A, Chapter 1, Section 7, d.

#### 3.3.9.8.2  Security Responsibilities

The DUAT Service must [1034] support the FAA to accomplish all of the tasks as defined in FAA Order 1370.82A, Chapter 2, Section 2. [1035].

# 4.0   rESERVED

# 5.0   Acronyms, Definitions, Glossary

See Section J3 of the Screening Information Request.

APPENDIX A

STATIC FLIGHT DATA

Because the actual amount of storage necessary to store the GFE static data is dependent on the implementation, the only sizing guidelines that can be given are for the input size of the weather data and the number of entries in the static data records.  The table below provides sizing guidelines for the static data.  Data size estimates for the weather data are incorporated in Appendix C.

Table A Static Flight Data

| Source | Updated (Days) | Subject | Minimum No. Items |
| --- | --- | --- | --- |
| NFDC | 56 | Airports | 18,812 |
| NFDC | 56 | NAVAIDs, Waypoints | 3,248 |
| NFDC | 56 | WX Reporting Locations | 1,966 |
| NFDC | 56 | Fixes | 16,605 |
| NFDC | 56 | Preferred Routes High | 1,835 |
| NFDC | 56 | Preferred Routes Low | 783 |
| NFDC | 56 | Jet Airways | 294 |
|  |  | Segments | 5,756 |
| NFDC | 56 | Victor Airways | 647 |
| AVN-460 | 90 | Pilots | 1,000,000 |
| NFDC | 56 | Colored Airways | 33 |
| ICAO (Montreal) | 365 | ICAO Data | 1,000,000 |
| NFDC | 56 | TEC Routes | 961 |
| NFDC | 56 | SIDs, STARS, and SIAPS | 486 |
| NFDC | 56 | Direct Routes Atlantic/Oceanic/SOCAL) | 750 |
| NFDC | 56 | ARTCC Boundaries | 13 |
| NFDC | 56 | Special Use Airways | 978 |

APPENDIX B

ADAPTABLE PARAMETERS

This table lists the adaptable parameters used in the specification.

Table B Adaptable Parameters

| Description | Parameter | Default Value | Minimum | Maximum | Incre-ment | Units |
| --- | --- | --- | --- | --- | --- | --- |
| Route Weather Corridor Width | RWXC | 50 | 10 | 100 | 5 | nm |
| Weather Search Area Radius | WXR | 25 | 10 | 100 | 5 | nm |
| Forecast Winds Aloft Corridor Width | FWAC | 200 | 100 | 600 | 50 | nm |
| Air Traffic Control Transmit Time | ATCTT | 60 | N/A | N/A | 10 | min |
| Flight Service Station Transmit Time | FSST | 30 | N/A | N/A | 10 | min |

APPENDIX C

40.   PRODUCT LISTING

This appendix contains a weather product listing.

| WEATHER TYPE | WX PROD ID | AREA/ POINT | RETENTION TIME | REPLACEMENT UPDATES | SOURCE | NUMBER OF REPORTS | AVERAGE SIZE (BYTES) | TRANS- MISSION TYPE | TIMES PER DAY | EST. TOTAL STORAGE REQ. (K BYTES) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ADVERSE CONDITIONS |  |
| Area Forecast | FA |  |  |  |  |  |  |  |  |  |
| Hazard/Flight Precautions | FA | A | 12 h | S | WMSCR* | 3 | 300 | S | 3 | 6 |
| Synopsis | FA | A | 12 h | S | WMSCR* | 10 | 1000 | S | 3 | 20 |
| Severe Weather Outlook | AC | A | 12 h | S | WMSCR* | 1 | 1600 | S | 2 | 2 |
| Severe WX Warning |  |  |  |  |  |  |  |  |  |  |
| Aviation Weather Alert Message | AWW | A | 6 h | U | WMSCR* | 1 | 150 | U | N/A | 2 |
| Severe WX Forecast | WW | A | 6 h | U | WMSCR* | 1 | 1200 | U | N/A | 10 |
| Severe WX Forecast Status | WW-A | A | 6 h | U | WMSCR* | 1 | 750 | U | N/A | 6 |
| Tropical Depression and Hurricane Advisory | WH | A | 6 h | U | WMSCR* | 3 | 1400 | U | N/A | 5 |
| Atlantic Ocean Tropical Cyclones | WTNT21-25 | A | 6 h | U | WMSCR* | 5 | 1400 | U | N/A | 7 |
| Pacific Ocean Tropical Cyclones (Marine Adv.) | WTPZ21-25 | A | 6 h | U | WMSCR* | 5 | 1400 | U | N/A | 7 |
| Atlantic Ocean Tropical Cyclones (Quick Change Updates) | WTNT61 | A | 6 h | U | WMSCR* | 3 | 1400 | U | N/A | 5 |
| Pacific Ocean Tropical Cyclones (Quick Change Updates) | WTPZ61 | A | 6 h | U | WMSCR* | 3 | 1400 | U | N/A | 5 |
| Atlantic Ocean Tropical Cyclones (Position Estimates) | WTNT51 | A | 6 h | U | WMSCR* | 3 | 1400 | U | N/A | 5 |
| Pacific Ocean Tropical Cyclones (Position Estimates) | WTPZ51 | A | 6 h | U | WMSCR* | 3 | 1400 | U | N/A | 5 |
| SIGMETs | WS | A | 4 h | R | WMSCR* | 99 | 100 | U | N/A | 14 |
| Convective SIGMET | WST | A | 4 h | R | WMSCR* | 3 | 400 | S | 24 | 2 |
| Center WX Advisory | CWA | A | 6 h | R | WMSCR* | 126 | 200 | U | N/A | 101 |
| Urgent WX Advisory | UCWA | A | 6 h | R/A | WMSCR* | 126 | 400 | U | N/A | 2 |
| AIRMET | WA | A | 6 h | R | WMSCR* | 30 | 1000 | U | N/A | 120 |
| CURRENT CONDITIONS |  |
| Surface Observation | SA | P | 185 m | A | WMSCR* | 2200 | 54 | S | 24 | 245 |
| Special Reports | SP | P | 185 m | A | WMSCR* | 2200 | 50 | U | N/A | 120 |
| Correction | COR | P | 185 m | A | WMSCR* | 200 | 50 | U | N/A | 35 |
| AMOS, AUTOB, RAMOS, ASOS, AWOS | SAME | P | 185 m | R | WMSCR* | 500 | 50 | S | N/A | 16 |
| Pilot Report | UA | P/A | 95 m | U | WMSCR* | 1600 | 75 | U | N/A | 117 |
| Urgent Pilot Report | UUA | P/A | 95 m | U | WMSCR* | 1600 | 75 | U | N/A | 90 |
| Radar Report | SD | A | 1 h | R | WMSCR* | 230 | 100 | U | N/A | 20 |
| Special Radar Report | SD-SPL | A | 1 h | R | WMSCR* | 230 | 70 |  | N/A | 0 7 |
| FORECAST CONDITIONS |  |
| Terminal Forecast | TAF | A | 18 h | R | WMSCR* | 1000 | 125 | S | 3 | 130 |
| TAF AMD | SAME | A | 18 h | R | WMSCR* | 1000 | 100 | U | N/A | 5 |
| WINDS ALOFT FORECAST |  |
| FD1 |  | FD | A | 18 h | R | WMSCR* | 400 | 70 | S | 2 | 29 |
| FD2 | LOW | FD | A | 18 h | R | WMSCR* | 400 | 70 | S | 2 | 29 |
| FD3 |  | FD | A | 18 h | R | WMSCR* | 400 | 70 | S | 2 | 29 |
| FD8 |  | FD | A | 18 h | R | WMSCR* | 100 | 20 | S | 2 | 2 |
| FD9 | HIGH | FD | A | 18 h | R | WMSCR* | 100 | 20 | S | 2 | 2 |
| FD10 |  | FD | A | 18 h | R | WMSCR* | 100 | 20 | S | 2 | 2 |
| Current Winds Aloft |  | FD | A | 18 h | R | WMSCR* | 100 | 20 | S | 2 | 2 |
| Grid Winds | GF | A | 18 h | R | WMSCR* | 3 | 1600 | S | 2 | 4 |
| Notice To Airmen | D | P | until exp. date | U | WMSCR* | 2200 | 40 | U | N/A | 88 |
| FDC NOTAMs | FDC | A | until exp. date | U | WMSCR* | 180 | 212 | U | N/A | 40 |
| LORAN NOTAMs | LORAN | A | until exp. time | U | WMSCR* | 100 | 50 | U | N/A | 20 |
| WAAS NOTAMs | WAAS | A | until exp. time | U | WMSCR* | 100 | 50 | U | N/A | 20 |
| GPS NOTAMs | GPS | A | until exp. time | U | WMSCR* | 100 | 50 | U | N/A | 20 |

| WEATHER TYPE | WX PROD ID | AREA/ POINT | RETENTION TIME | REPLACEMENT UPDATES | SOURCE | NUMBER OF REPORTS | AVERAGE SIZE (BYTES) | TRANS- MISSION TYPE | TIMES PER DAY | EST. TOTAL STORAGE REQ. (K BYTES) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ATCSCC Delay Info | ATC | A | until exp. date | U | Govt Approved source | 75 | 100 | U | N/A | 5 |
| ATCSCC Warning Restricted Areas | WRS | A | until exp. date | U | Govt Approved source | 100 | 100 | U | N/A | 1 |
| GRAPHIC PRODUCTS |  |
| Surface Analysis |  | A | 3 h | R | Govt Approved source | 1 | 477 K | S | 8 | 954 K |
| Weather Depiction |  | A | 3 h | R | Govt Approved source | 1 | 230 K | S | 8 | 460 K |
| Radar Summary/NEXRAD |  | A | 1 h | R | Govt Approved source | 1 | 232 K | S | 24 | 464 K |
| Low-Level Significant Weather Prognosis |  | A | 6 h | R | Govt Approved source | 1 | 256 K | S | 4 | 512 K |
| High-Level Significant Weather Prognosis |  | A | 6 h | R | Govt Approved source | 1 | 256 K | S | 4 | 512 K |
| Composite Moisture Stability Chart (Stability Panel only) |  | A | 12 h | R | Govt Approved source | 1 | 203 K | S | 2 | 406 K |
| Severe Weather Outlook |  | A | 24 h | R | Govt Approved source | 1 | 183 K | S | 1 | 366 K |
| Constant Pressure Charts 850/700/500/300/200mb | mb |  |  | U | Govt Approved source | 1 | 750 K |  | N/A |  |
| 36 and 48 hour surface prognosis |  | A | 6h | R | Govt Approved source | 1 | 256K | S | 4 | 512K |
| Satellite Imagery |  |  |  | U | Govt Approved source | 1 | 750 K |  | N/A |  |

Legend:

Area/Point:  A = Area,  P = Point

Replacement Updates: A = Appended R = Replaced S = Scheduled U = Unscheduled

Transmission Type: S = Scheduled U = Unscheduled

Size:  K = Kilobytes, M = Megabytes

Time:  h = hours, m = minutes

____________

* Or other comparable system or service.

APPENDIX D

Reserved

Appendix E

VERIFICATION REQUIREMENTS TRACEABILITY MATRIX (VRTM)

Table E contains the DUAT Service VRTM.  The test methods identified are:

I  = Inspection

A  = Analysis

D  = Demonstration

T  = Test

T/A = Test and Analysis

Table E  DUAT Service VRTM

| Specification Paragraph | Rqmt No. | Ver Method |  |
| --- | --- | --- | --- |
| 3.0 REQUIREMENTS | --- | --- |  |
| 3.1 Definition | --- | --- |  |
| 3.2 Characteristics | --- | --- |  |
| 3.2.1 Functional Characteristics | 001 | D |  |
| 3.2.1 Functional Characteristics | 002 | D |  |
| 3.2.1 Functional Characteristics | 003 | D |  |
| 3.2.1 Functional Characteristics | 004 | D |  |
| 3.2.1 Functional Characteristics | 005 | D |  |
| 3.2.1 Functional Characteristics | 006 | D |  |
| 3.2.1 Functional Characteristics (Internet Interface) | 810 | D |  |
| 3.2.1.1 General Requirements | 007 | D |  |
| 3.2.1.1 General Requirements | 008 | D |  |
| 3.2.1.1 General Requirements | 009 | D |  |
| 3.2.1.1 General Requirements | 010 | D |  |
| 3.2.1.1 General Requirements | 011 | D |  |
| 3.2.1.1 General Requirements | 012 | D |  |
| 3.2.1.1 General Requirements | 013 | D |  |
| 3.2.1.1 General Requirements | 014 | D |  |
| 3.2.1.1 General Requirements | 015 | D |  |
| 3.2.1.1 General Requirements | 016 | D |  |
| 3.2.1.1 General Requirements | 017 | D |  |
| 3.2.1.1 General Requirements | 018 | D |  |
| 3.2.1.1 General Requirements | 019 | D |  |
| 3.2.1.1 General Requirements | 020 | D |  |
| 3.2.1.1 General Requirements | 021 | D |  |
| 3.2.1.1 General Requirements | 022 | D |  |
| 3.2.1.1 General Requirements | 023 | D |  |
| 3.2.1.1 General Requirements | 024 | D |  |
| 3.2.1.1 General Requirements | 025 | D |  |
| 3.2.1.1 General Requirements | 026 | D |  |
| 3.2.1.1 General Requirements | 811 | D |  |
| 3.2.1.1 General Requirements | 812 | D |  |
| 3.2.1.1.1 Data Entry and Formats | 705 | I |  |
| 3.2.1.1.2 Airport Diagrams | 706 | I |  |
| 3.2.1.1.3 Military Graphical Data | 920 | I |  |
| 3.2.1.2 Range of Service | -- | -- |  |
| 3.2.1.2.1 Weather Briefing and Flight Planning | 027 | D |  |
| 3.2.1.2.1 Weather Briefing and Flight Planning | 028 | D |  |
| 3.2.1.2.1.1 Reserved | --- | --- |  |
| 3.2.1.2.2 International Weather Support | 029 | D |  |
| 3.2.1.2.2 International Weather Support | 030 | D |  |
| 3.2.1.2.2 International Weather Support | 031 | D |  |
| 3.2.1.2.2 International Weather Support | 032 | D |  |
| 3.2.1.2.2 International Weather Support | 033 | D |  |
| 3.2.1.2.2 International Weather Support | 034 | D |  |
| 3.2.1.2.2 International Weather Support | 035 | D |  |
| 3.2.1.2.2 International Weather Support | 036 | D |  |
| 3.2.1.2.2 International Weather Support | 037 | D |  |
| 3.2.1.2.2 International Weather Support | 038 | D |  |
| 3.2.1.2.2 International Weather Support | 750 | D |  |
| 3.2.1.3 Source Data and Database Maintenance | --- | --- |  |
| 3.2.1.3.1 Authorized Users | 041 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 070 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 072 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 910 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 911 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 912 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 913 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 914 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 915 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 923 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 924 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 925 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 926 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 927 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 928 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 929 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 930 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 931 | D |  |
| 3.2.1.3.1.1 Graphic Weather Data | 813 | D |  |
| 3.2.1.3.2 Static Flight Data | 042 | D |  |
| 3.2.1.3.2 Static Flight Data | 043 | D |  |
| 3.2.1.3.2 Static Flight Data | 044 | D |  |
| 3.2.1.3.2.1 Data Availability | 045 | D |  |
| 3.2.1.3.2.2 Editing and Error Correction | 046 | D |  |
| 3.2.1.3.2.2 Editing and Error Correction | 047 | D |  |
| 3.2.1.3.2.3 Characteristics | 048 | I |  |
| 3.2.1.3.3 Dynamic Weather and NOTAM Data | 049 | A |  |
| 3.2.1.3.3 Dynamic Weather and NOTAM Data | 039 | A |  |
| 3.2.1.3.3.1 Weather and NOTAM Products | 050 | I |  |
| 3.2.1.3.3.1 Weather and NOTAM Products | 051 | I |  |
| 3.2.1.3.3.1.1 Full Text Products | 052 | D |  |
| 3.2.1.3.3.1.1 Full Text Products | 053 | D |  |
| 3.2.1.3.3.2 ICAO Weather Codes | 054 | D |  |
| 3.2.1.3.3.2 ICAO Weather Codes | 055 | D |  |
| 3.2.1.3.3.2 ICAO Weather Codes | 056 | D |  |
| 3.2.1.3.3.2 ICAO Weather Codes (Canadian FAs) | 830 | D |  |
| 3.2.1.3.3.3 Surface Weather Observations | --- | --- |  |
| 3.2.1.3.3.4 Data Retention | 057 | D |  |
| 3.2.1.3.3.4.1 Data Purge | 060 | D |  |
| 3.2.1.3.3.4.1 Data Purge | 061 | D |  |
| 3.2.1.3.3.4.1 Data Purge | 062 | D |  |
| 3.2.1.3.3.4.1 Data Purge | 063 | D |  |
| 3.2.1.3.3.5 Corrected or Amended Weather Products | 064 | D |  |
| 3.2.1.3.3.5 Corrected or Amended Weather Products | 065 | D |  |
| 3.2.1.3.3.6 Reserved | --- | --- |  |
| 3.2.1.3.3.7. Routine Delay Weather Products | 066 | D |  |
| 3.2.1.4 Processing Requirements | 932 | I |  |
| 3.2.1.4.1. Database Maintenance | --- | --- |  |
| 3.2.1.4.1.1 Alphanumeric Weather Data | 067 | D |  |
| 3.2.1.4.1.1 Alphanumeric Weather Data | 068 | D |  |
| 3.2.1.4.1.1 Alphanumeric Weather Data | 069 | D |  |
| 3.2.1.4.1.2 Reserved | --- | --- |  |
| 3.2.1.4.1.3 Static Flight Data | 074 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 075 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 076 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 077 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 078 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 079 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 080 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 081 | D |  |
| 3.2.1.4.1.3 Static Flight Data | 083 | D |  |
| 3.2.1.4.1.4 User Directory Assistance | 820 | D |  |
| 3.2.1.4.1.4 User Directory Assistance | 821 | D |  |
| 3.2.1.4.2 Weather Message Identification | 084 | D |  |
| 3.2.1.4.2 Weather Message Identification | 085 | D |  |
| 3.2.1.4.2.1 Weather Message Text Editing | 086 | D |  |
| 3.2.1.4.2.2 Weather Message Duplication | 087 | D |  |
| 3.2.1.4.3 Weather Information Function | --- | --- |  |
| 3.2.1.4.3.1 Weather Briefing Formats | 088 | D |  |
| 3.2.1.4.3.1 Weather Briefing Formats | 089 | D |  |
| 3.2.1.4.3.1 Weather Briefing Formats | 090 | D |  |
| 3.2.1.4.3.1.1 Standard Weather Briefing | 091 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 092 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 093 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 094 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 095 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 096 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 097 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 098 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 099 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 100 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 101 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 102 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 103 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 104 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 105 | D |  |
| 3.2.1.4.3.1.1.1 Input (Standard Weather Briefing) | 106 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 107 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 108 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 109 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 110 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 111 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 112 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 113 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 114 | D |  |
| 3.2.1.4.3.1.1.2 Output (Standard Weather Briefing) | 115 | D |  |
| 3.2.1.4.3.1.2 Abbreviated Weather Briefing | 116 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 117 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 118 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 119 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 120 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 121 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 122 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 123 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 761 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 762 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 763 | D |  |
| 3.2.1.4.3.1.2.1 Input (Abbreviated Weather Briefing) | 764 | D |  |
| 3.2.1.4.3.1.2.2 Output (Abbreviated Weather Briefing) | 124 | D |  |
| 3.2.1.4.3.1.3 Outlook Weather Briefing | 125 | D |  |
| 3.2.1.4.3.1.3.1 Input (Outlook Weather Briefing) | 126 | D |  |
| 3.2.1.4.3.1.3.2 Output (Outlook Weather Briefing) | 127 | D |  |
| 3.2.1.4.3.1.3.2 Output (Outlook Weather Briefing) | 128 | D |  |
| 3.2.1.4.3.1.3.2 Output (Outlook Weather Briefing) | 129 | D |  |
| 3.2.1.4.3.1.3.2 Output (Outlook Weather Briefing) | 130 | D |  |
| 3.2.1.4.3.1.3.2 Output (Outlook Weather Briefing) | 131 | D |  |
| 3.2.1.4.3.2 Adverse Weather Products | --- | --- |  |
| 3.2.1.4.3.2 1 Standard and Outlook Weather Briefings | 132 | D |  |
| 3.2.1.4.3.2.1.1 Tropical Advisories | 133 | D |  |
| 3.2.1.4.3.2.1.2 Reserved | --- | --- |  |
| 3.2.1.4.3.2.1.3 Severe Weather Outlook | 134 | D |  |
| 3.2.1.4.3.2.1.3 Severe Weather Outlook | 765 | D |  |
| 3.2.1.4.3.2.2 Abbreviated Weather Briefing | 135 | D |  |
| 3.2.1.4.3.2.2 Abbreviated Weather Briefing | 136 | D |  |
| 3.2.1.4.3.2.3 Area Forecast Output | 137 | D |  |
| 3.2.1.4.3.3 Trend Weather Products | 138 | D |  |
| 3.2.1.4.3.3.1 Trend Weather Product Requests | 139 | D |  |
| 3.2.1.4.3.4 Forecast Winds and Temperature Aloft | 140 | D |  |
| 3.2.1.4.3.4 Forecast Winds and Temperature Aloft | 141 | D |  |
| 3.2.1.4.3.4 Forecast Winds and Temperature Aloft | 142 | D |  |
| 3.2.1.4.3.4 Forecast Winds and Temperature Aloft | 143 | D |  |
| 3.2.1.4.3.4.1 Output Time Period | 144 | D |  |
| 3.2.1.4.3.4.1 Output Time Period | 145 | D |  |
| 3.2.1.4.3.5 Alternate Airport Weather | 146 | D |  |
| 3.2.1.4.3.5 Alternate Airport Weather | 147 | D |  |
| 3.2.1.4.3.5 Alternate Airport Weather | 148 | D |  |
| 3.2.1.4.3.5 Alternate Airport Weather | 149 | D |  |
| 3.2.1.4.3.5 Alternate Airport Weather | 150 | D |  |
| 3.2.1.4.3.6 Closest Reporting Location | 151 | D |  |
| 3.2.1.4.3.6 Closest Reporting Location | 152 | D |  |
| 3.2.1.4.3.6 Closest Reporting Location | 153 | D |  |
| 3.2.1.4.3.6 Closest Reporting Location | 154 | D |  |
| 3.2.1.4.3.7 Collective Products | 155 | D |  |
| 3.2.1.4.3.8 Weather Briefing Entry Carryover | 156 | D |  |
| 3.2.1.4.3.9 Use of Previous Route | 157 | D |  |
| 3.2.1.4.3.9 Use of Previous Route | 158 | D |  |
| 3.2.1.4.3.10 Reserved | --- | --- |  |
| 3.2.1.4.3.11 Product Retrieval | --- | --- |  |
| 3.2.1.4.3.11.1 Weather Product Search Area | 187 | D |  |
| 3.2.1.4.3.11.1 Weather Product Search Area | 188 | D |  |
| 3.2.1.4.3.11.2 Retrieval Processing | 189 | D |  |
| 3.2.1.4.3.12 NOTAMs | 190 | D |  |
| 3.2.1.4.3.12 NOTAMs | 191 | D |  |
| 3.2.1.4.3.12.1 Non-associated Facilities | 192 | D |  |
| 3.2.1.4.3.12.2 Reserved | --- | --- |  |
| 3.2.1.4.3.13 Graphical TFRs | 767 | D |  |
| 3.2.1.4.3.14 Superseded Products | 193 | D |  |
| 3.2.1.4.3.14 Superseded Products | 194 | D |  |
| 3.2.1.4.3.15 DUAT Service Interruptions | --- | --- |  |
| 3.2.1.4.3.15.1 Short-Term Weather Data Interruption | 195 | D |  |
| 3.2.1.4.3.15.1 Short-Term Weather Data Interruption | 196 | D |  |
| 3.2.1.4.3.15.1.1 Short-Term Interruption Message | 197 | D |  |
| 3.2.1.4.3.15.1.1 Short-Term Interruption Message | 198 | D |  |
| 3.2.1.4.3.15.1.1 Short-Term Interruption Message | 199 | D |  |
| 3.2.1.4.3.15.1.2 Short-Term Interruption Resumption | 200 | I |  |
| 3.2.1.4.3.15.1.2 Short-Term Interruption Resumption | 201 | I |  |
| 3.2.1.4.3.15.2 Long-Term Weather Data Interruption | 202 | D |  |
| 3.2.1.4.3.15.2 Long-Term Weather Data Interruption | 203 | D |  |
| 3.2.1.4.3.15.2.1 Long-Term Interruption Message | 204 | D |  |
| 3.2.1.4.3.15.2.2 Long-Term Interruption Resumption | 205 | A |  |
| 3.2.1.4.3.15.2.2 Long-Term Interruption Resumption | 206 | I |  |
| 3.2.1.4.3.15.2.2 Long-Term Interruption Resumption | 207 | I |  |
| 3.2.1.4.3.15.3 USNS-R Interruption | 208 | D |  |
| 3.2.1.4.3.15.3 USNS-R Interruption | 209 | A |  |
| 3.2.1.4.3.15.4 DUAT Service System Failure | 210 | I |  |
| 3.2.1.4.3.15.4 DUAT Service System Failure | 211 | I |  |
| 3.2.1.4.3.15.4.1 DUAT Data Base Rebuild | 212 | I |  |
| 3.2.1.4.3.15.4.2 DUAT System Failure Message | 213 | D |  |
| 3.2.1.4.3.16 Unavailable Weather Products | --- | --- |  |
| 3.2.1.4.3.16.1 Product Not in the Database | 214 | D |  |
| 3.2.1.4.3.16.2 Invalid Product | 215 | D |  |
| 3.2.1.4.3.16.3 Invalid Format | 216 | D |  |
| 3.2.1.4.4 Flight Planning Function | 217 | D |  |
| 3.2.1.4.4 Flight Planning Function | 218 | D |  |
| 3.2.1.4.4 Flight Planning Function | 219 | D |  |
| 3.2.1.4.4 Flight Planning Function | 220 | D |  |
| 3.2.1.4.4 Flight Planning Function | 221 | D |  |
| 3.2.1.4.4.1 Flight Planning Software Capabilities | 825 | D |  |
| 3.2.1.4.4.1 Flight Planning Software Capabilities | 826 | D |  |
| 3.2.1.4.4.1 Flight Planning Software Capabilities | 827 | D |  |
| 3.2.1.4.4.1 Flight Planning Software Capabilities | 828 | D |  |
| 3.2.1.4.4.1 Flight Planning Software Capabilities | 829 | D |  |
| 3.2.1.4.4.2 Stored Flight Plans | 222 | D |  |
| 3.2.1.4.4.2 Stored Flight Plans | 701 | D |  |
| 3.2.1.4.4.2 Stored Flight Plans | 751 | D |  |
| 3.2.1.4.4.2 Stored Flight Plans | 752 | D |  |
| 3.2.1.4.4.2 Stored Flight Plans | 753 | D |  |
| 3.2.1.4.4.2 Stored Flight Plans | 703 | D/A |  |
| 3.2.1.4.4.3 Message Formatting | 223 | D |  |
| 3.2.1.4.4.3 Message Formatting | 224 | D |  |
| 3.2.1.4.4.3 Message Formatting | 225 | D |  |
| 3.2.1.4.4.3.1 Flight Data Message Precedence | 226 | D |  |
| 3.2.1.4.4.3.1 Flight Data Message Precedence | 227 | D |  |
| 3.2.1.4.4.4 Flight Plan Processing | 229 | D |  |
| 3.2.1.4.4.4.1 Domestic Flight Plan Processing | 230 | D |  |
| 3.2.1.4.4.4.1 Domestic Flight Plan Processing | 231 | D |  |
| 3.2.1.4.4.4.2 ICAO Flight Plan Processing | 233 | D |  |
| 3.2.1.4.4.4.2 ICAO Flight Plan Processing | 234 | D |  |
| 3.2.1.4.4.4.2 ICAO Flight Plan Processing | 235 | D |  |
| 3.2.1.4.4.4.3 Adverse Weather Conditions | 236 | D |  |
| 3.2.1.4.4.4.3 Adverse Weather Conditions | 237 | D |  |
| 3.2.1.4.4.5 Acknowledgments | 238 | D |  |
| 3.2.1.4.4.5 Acknowledgments | 239 | D |  |
| 3.2.1.4.4.6 IFR Flight Plans | 240 | D |  |
| 3.2.1.4.4.6 IFR Flight Plans | 241 | D |  |
| 3.2.1.4.4.6 IFR Flight Plans | 768 | D |  |
| 3.2.1.4.4.6.1 IFR Parameter Time | 242 | D |  |
| 3.2.1.4.4.6.1 IFR Parameter Time | 243 | D |  |
| 3.2.1.4.4.7 Domestic and ICAO VFR Flight Plans | 244 | D |  |
| 3.2.1.4.4.7 Domestic and ICAO VFR Flight Plans | 245 | D |  |
| 3.2.1.4.4.7.1 Domestic and ICAO VFR Parameter Time | 246 | D |  |
| 3.2.1.4.4.7.1 Domestic and ICAO VFR Parameter Time | 247 | D |  |
| 3.2.1.4.4.8 Alaska Flight Plans | 248 | D |  |
| 3.2.1.4.4.9 File Flight Plan with ARTCC | 249 | D |  |
| 3.2.1.4.4.9 File Flight Plan with ARTCC | 250 | D |  |
| 3.2.1.4.4.9 File Flight Plan with ARTCC | 251 | D |  |
| 3.2.1.4.4.9 File Flight Plan with ARTCC | 252 | D |  |
| 3.2.1.4.4.10 Multiple Flight Plans | 253 | D |  |
| 3.2.1.4.4.10.1 Dispatcher Flight Plans | 254 | D |  |
| 3.2.1.4.4.10.1 Dispatcher Flight Plans | 255 | D |  |
| 3.2.1.4.4.11 Formatted Flight Plans | 259 | D |  |
| 3.2.1.4.4.11 Formatted Flight Plans | 260 | D |  |
| 3.2.1.4.4.11 Formatted Flight Plans | 261 | D |  |
| 3.2.1.4.4.12 Data Transmission | 262 | D |  |
| 3.2.1.4.4.13 Flight Plan Storage | --- | --- |  |
| 3.2.1.4.4.13.1 IFR Flight Plan Storage | 263 | D |  |
| 3.2.1.4.4.13.1 IFR Flight Plan Storage | 264 | D |  |
| 3.2.1.4.4.13.2 VFR Flight Plan Storage | 265 | D |  |
| 3.2.1.4.4.13.2 VFR Flight Plan Storage | 266 | D |  |
| 3.2.1.4.4.14 Time Modifications | 267 | D |  |
| 3.2.1.4.4.15 Duplicate Flight Plans | 268 | D |  |
| 3.2.1.4.4.15 Duplicate Flight Plans | 269 | D |  |
| 3.2.1.4.4.16 Flight Plan Acknowledgements | --- | --- |  |
| 3.2.1.4.4.16.1 IFR Acknowledgment | 270 | D |  |
| 3.2.1.4.4.16.1 IFR Acknowledgment | 272 | D |  |
| 3.2.1.4.4.16.2 VFR Acknowledgment | 276 | D |  |
| 3.2.1.4.4.16.2 VFR Acknowledgment | 278 | D |  |
| 3.2.1.4.4.17 Error/Reject Messages | --- | --- |  |
| 3.2.1.4.4.17.1 Error Message Procedures | 280 | D |  |
| 3.2.1.4.4.17.1 Error Message Procedures | 281 | D |  |
| 3.2.1.4.4.17.1 Error Message Procedures | 282 | D |  |
| 3.2.1.4.4.17.1 Error Message Procedures | 283 | D |  |
| 3.2.1.4.4.17.2 Reject Message Procedures | 284 | D |  |
| 3.2.1.4.4.17.2 Reject Message Procedures | 285 | D |  |
| 3.2.1.4.4.17.2 Reject Message Procedures | 286 | D |  |
| 3.2.1.4.4.17.2 Reject Message Procedures | 287 | D |  |
| 3.2.1.4.4.18 Flight Plan Filing | 288 | D |  |
| 3.2.1.4.4.18 Flight Plan Filing | 040 | D |  |
| 3.2.1.4.4.18 Flight Plan Filing | 058 | D |  |
| 3.2.1.4.4.18 Flight Plan Filing | 059 | D |  |
| 3.2.1.4.4.19 Lifeguard Flights | 289 | D |  |
| 3.2.1.4.4.20 Flight Plan Input | 290 | D |  |
| 3.2.1.4.4.20.1 Domestic Flight Plan Acceptance | 291 | D |  |
| 3.2.1.4.4.20.2 ICAO Flight Plan Acceptance | 292 | D |  |
| 3.2.1.4.4.20.3 Incorrect Entries | 293 | D |  |
| 3.2.1.4.4.20.4 Format Checking | 294 | D |  |
| 3.2.1.4.4.20.4 Format Checking | 295 | D |  |
| 3.2.1.4.4.20.5 Latitude-Longitude Entry | 296 | D |  |
| 3.2.1.4.4.20.5 Latitude-Longitude Entry | 297 | D |  |
| 3.2.1.4.4.20.6 Washington, DC Metropolitan Area Flight Restricted Zone (DC FRZ) | 071 | D |  |
| 3.2.1.4.4.21 Flight Plan Display | 298 | D |  |
| 3.2.1.4.4.21.1 Flight Plan Modification/Filing | 299 | D |  |
| 3.2.1.4.4.21.1 Flight Plan Modification/Filing | 300 | D |  |
| 3.2.1.4.4.21.1.1 Weather Briefing Update | 301 | D |  |
| 3.2.1.4.4.21.1.2 Re-output Modified Flight Plan | 303 | D |  |
| 3.2.1.4.4.21.1.3 Continuation of Changes | 304 | D |  |
| 3.2.1.4.4.21.1.3 Continuation of Changes | 305 | D |  |
| 3.2.1.4.4.21.1.3 Continuation of Changes | 306 | D |  |
| 3.2.1.4.4.22 Completion Message | 307 | D |  |
| 3.2.1.4.4.23 Reserved |  |  |  |
| 3.2.1.4.4.24 Route Definition | 308 | D |  |
| 3.2.1.4.4.24 Route Definition | 309 | D |  |
| 3.2.1.4.4.24 Route Definition | 310 | D |  |
| 3.2.1.4.4.24 Route Definition | 311 | D |  |
| 3.2.1.4.4.24 Route Definition | 312 | D |  |
| 3.2.1.4.4.24 Route Definition | 313 | D |  |
| 3.2.1.4.4.24 Route Definition | 315 | D |  |
| 3.2.1.4.4.24 Route Definition | 316 | D |  |
| 3.2.1.4.4.24 Route Definition | 317 | D |  |
| 3.2.1.4.4.24 Route Definition | 318 | D |  |
| 3.2.1.4.4.24.1 Valid Elements and Fixes | 319 | D |  |
| 3.2.1.4.4.24.2 Route Contiguous Legs | 320 | D |  |
| 3.2.1.4.4.24.3 Previously Entered Data | 321 | D |  |
| 3.2.1.4.4.24.4 Preferred Routes | 322 | D |  |
| 3.2.1.4.4.24.4 Preferred Routes | 323 | D |  |
| 3.2.1.4.4.24.4 Preferred Routes | 324 | D |  |
| 3.2.1.4.4.24.4.1 Preferred Route Selection | 326 | D |  |
| 3.2.1.4.4.24.4.1 Preferred Route Selection | 327 | D |  |
| 3.2.1.4.4.24.4.1 Application of Preferred Routes | 328 | D |  |
| 3.2.1.4.4.24.4.1 Application of Preferred Routes | 329 | D |  |
| 3.2.1.4.4.25 Flight Plan Amendments/Cancellations | 330 | D |  |
| 3.2.1.4.4.25 Flight Plan Amendments/Cancellations | 331 | D |  |
| 3.2.1.4.4.25.1 Authorization | 332 | D |  |
| 3.2.1.4.4.25.1 Authorization | 333 | D |  |
| 3.2.1.4.4.25.2 Flight Plan Retrieval | 334 | D |  |
| 3.2.1.4.4.25.2 Flight Plan Retrieval | 335 | D |  |
| 3.2.1.4.4.25.3 Flight Plan Amendments | 336 | D |  |
| 3.2.1.4.4.25.3.1 Flight Plan Time Limits | 337 | D |  |
| 3.2.1.4.4.26 Flight Plan Entry Carryover | 338 | D |  |
| 3.2.1.4.4.27 Acceptance Messages | 339 | D |  |
| 3.2.1.4.4.28 Cancel Flight Plans | --- | --- |  |
| 3.2.1.4.4.28.1 Flight Plan Retention | 340 | D |  |
| 3.2.1.4.4.28.2 Time for Cancellation | 341 | D |  |
| 3.2.1.4.4.28.3 Message After Cancellation | 342 | D |  |
| 3.2.1.4.4.28.4 Notification of Transmission | 343 | D |  |
| 3.2.1.4.4.28.5 No Flight Plan Message | 344 | D |  |
| 3.2.1.4.4.29 VFR Flight Plan Closure | 345 | D |  |
| 3.2.1.4.4.29 VFR Flight Plan Closure | 346 | D |  |
| 3.2.1.4.4.29.1 Flight Plan Closure Acceptance | 347 | D |  |
| 3.2.1.4.4.29.1 Flight Plan Closure Acceptance | 348 | D |  |
| 3.2.1.4.4.29.1.1 Required Entries | 349 | D |  |
| 3.2.1.4.4.29.1.1 Required Entries | 350 | D |  |
| 3.2.1.4.4.29.1.1 Required Entries | 351 | D |  |
| 3.2.1.4.4.29.1.1 Required Entries | 352 | D |  |
| 3.2.1.4.4.29.1.1 Required Entries | 353 | D |  |
| 3.2.1.4.4.29.2 Closure Message | 354 | D |  |
| 3.2.1.4.4.29.2 Closure Message | 355 | D |  |
| 3.2.1.4.4.29.3 Receipt of Closure Message | 356 | D |  |
| 3.2.1.4.4.29.3 Receipt of Closure Message | 357 | D |  |
| 3.2.1.4.4.29.4 Acknowledgment | 358 | D |  |
| 3.2.1.4.4.30 Traffic Management Function | 360 | D |  |
| 3.2.1.4.4.30 Traffic Management Function | 361 | D |  |
| 3.2.1.4.4.30 Traffic Management Function | 362 | D |  |
| 3.2.1.4.4.31 Encode/Decode Functions | 363 | D |  |
| 3.2.1.4.4.31 Encode/Decode Functions | 364 | D |  |
| 3.2.1.4.4.31 Encode/Decode Functions | 365 | D |  |
| 3.2.1.4.4.31 Encode/Decode Functions | 366 | D |  |
| 3.2.1.4.4.31.1 Domestic Location Information | 367 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 368 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 369 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 370 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 371 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 372 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 373 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 374 | D |  |
| 3.2.1.4.4.31.2 ICAO Area of Responsibility | 375 | D |  |
| 3.2.1.4.4.32 Escape to Encode/Decode Function | 376 | D |  |
| 3.2.1.4.4.32 Escape to Encode/Decode Function | 377 | D |  |
| 3.2.1.4.4.33 Data Recording and Retention | --- | --- |  |
| 3.2.1.4.4.33.1 Event Recording and Reconstruction | 378 | D |  |
| 3.2.1.4.4.33.1 Event Recording and Reconstruction | 379 | D |  |
| 3.2.1.4.4.33.1.1 Transaction Recording | 380 | D |  |
| 3.2.1.4.4.33.1.1 Transaction Recording | 381 | D |  |
| 3.2.1.4.4.33.1.1 Transaction Recording | 382 | D |  |
| 3.2.1.4.4.33.1.2 Event Reconstruction | 383 | D |  |
| 3.2.1.4.4.33.1.2 Event Reconstruction | 384 | D |  |
| 3.2.1.4.4.33.1.2 Event Reconstruction | 704 | D |  |
| 3.2.1.4.4.33.1.2 Event Reconstruction | 385 | D |  |
| 3.2.1.4.4.33.1.2.1 Event Retrieval Key | 386 | D |  |
| 3.2.1.4.4.33.1.2.2 Event Retrieval Time Period | 387 | D |  |
| 3.2.1.4.4.33.1.2.2 Event Retrieval Time Period | 388 | D |  |
| 3.2.1.4.4.33.1.3 Transaction Data Retention | 389 | D |  |
| 3.2.1.4.4.33.1.3 Transaction Data Retention | 390 | D |  |
| 3.2.1.4.4.33.2 Incoming Weather and NOTAM Data | 391 | D |  |
| 3.2.1.4.4.33.2 Incoming Weather and NOTAM Data | 393 | D |  |
| 3.2.1.4.4.33.2.1 Weather and NOTAM Data Recording | 394 | D |  |
| 3.2.1.4.4.33.2.1 Weather and NOTAM Data Recording | 395 | D |  |
| 3.2.1.4.4.33.2.2 Weather and NOTAM Data Retention | 396 | D |  |
| 3.2.1.4.4.33.2.2 Weather and NOTAM Data Retention | 397 | D |  |
| 3.2.1.4.4.33.2.3 Data Retrieval | 398 | D |  |
| 3.2.1.4.4.33.2.3 Data Retrieval | 399 | D |  |
| 3.2.1.4.4.33.2.3 Data Retrieval | 400 | D |  |
| 3.2.1.4.4.33.2.3 Data Retrieval | 401 | D |  |
| 3.2.1.4.4.33.2.3 Data Retrieval | 402 | D |  |
| 3.2.1.4.4.33.2.3 Data Retrieval | 403 | D |  |
| 3.2.1.4.4.33.2.3.1 Time-Stamp Display | 404 | D |  |
| 3.2.1.4.4.33.2.3.1 Time-Stamp Display | 405 | D |  |
| 3.2.1.4.4.33.2.3.1 Time-Stamp Display | 406 | D |  |
| 3.2.1.4.4.33.3 Event Reconstruction Requests | 407 | D |  |
| 3.2.1.4.4.33.3.1 Request Response Time | 414 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 415 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 416 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 417 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 418 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 419 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 420 | D |  |
| 3.2.1.4.4.34 Search and Rescue Requests (SAR) | 1046 | D |  |
| 3.2.1.4.4.34.1 SAR Response Time | 421 | D |  |
| 3.2.1.4.4.34.1 SAR Response Time | 422 | D |  |
| 3.2.1.4.4.34.2 SAR Response Order | 423 | D |  |
| 3.2.1.4.4.34.3 Data Search | 424 | D |  |
| 3.2.1.4.4.34.3.1 Continuation of Search | 425 | D |  |
| 3.2.1.4.4.34.4 Data Retrieval | 426 | D |  |
| 3.2.1.4.4.34.4 Data Retrieval | 427 | D |  |
| 3.2.1.4.4.34.4 Data Retrieval | 428 | D |  |
| 3.2.1.4.4.34.5 Response Data | 429 | D |  |
| 3.2.1.4.4.34.5 Response Data | 430 | D |  |
| 3.2.1.4.4.34.5 Response Data | 431 | D |  |
| 3.2.1.4.4.34.5 Response Data | 432 | D |  |
| 3.2.1.4.4.34.6 No Data Found in Search | 433 | D |  |
| 3.2.1.4.4.34.6 No Data Found in Search | 434 | D |  |
| 3.2.1.4.5 DUAT Service Access | 435 | T/A |  |
| 3.2.1.4.5.1 Transaction Provisions | 437 | D |  |
| 3.2.1.4.5.1.1 Time Recording Accuracy | 438 | D |  |
| 3.2.1.4.5.1.2 User Time Warnings | 439 | D |  |
| 3.2.1.4.5.2. Termination | --- | --- |  |
| 3.2.1.4.5.2.1 Transaction Termination | 440 | D |  |
| 3.2.1.4.5.2.2 Time-out Termination | 441 | D |  |
| 3.2.1.4.5.2.2.1 Time-out | 442 | D |  |
| 3.2.1.4.5.2.2.2 Reserved | --- | --- |  |
| 3.2.1.4.5.2.2.3 Termination Disconnect | 443 | D |  |
| 3.2.1.4.5.3 Transaction Number | 444 | D |  |
| 3.2.1.4.5.3.1 Sequence Assignment | 445 | D |  |
| 3.2.1.4.5.3.2 Storage | 447 | D |  |
| 3.2.1.4.6 User Information | --- | --- |  |
| 3.2.1.4.6.1 FAA Information | 448 | D |  |
| 3.2.1.4.6.1 FAA Information | 449 | D |  |
| 3.2.1.4.6.1 FAA Information | 450 | D |  |
| 3.2.1.4.6.2 Input Error Detection | 460 | D |  |
| 3.2.1.4.6.2.1 Reentering Data | 461 | D |  |
| 3.2.1.4.6.3 Date and Time Display | 462 | D |  |
| 3.2.1.4.6.3 Date and Time Display | 463 | D |  |
| 3.2.1.4.7 Help Function | 464 | D |  |
| 3.2.1.4.7.1 Help Function Field Entries | 465 | D |  |
| 3.2.1.4.7.1 Help Function Field Entries | 466 | D |  |
| 3.2.1.4.7.1 Help Function Field Entries | 467 | D |  |
| 3.2.1.4.7.2 Access to Help Function | 468 | D |  |
| 3.2.1.4.7.3 Expanded Help Function | 469 | D |  |
| 3.2.1.4.7.3 Expanded Help Function | 470 | D |  |
| 3.2.1.4.7.3 Expanded Help Function | 471 | D |  |
| 3.2.1.4.7.3 Expanded Help Function | 472 | D |  |
| 3.2.1.4.7.4 ICAO Help Function | 473 | D |  |
| 3.2.1.4.7.4.1 ICAO Help Function Entry | 474 | D |  |
| 3.2.1.4.8 DUAT Service Help Line | 475 | D |  |
| 3.2.1.4.8 DUAT Service Help Line (Assist Internet Interface) | 1040 | D |  |
| 3.2.1.4.8 DUAT Service Help Line | 476 | D |  |
| 3.2.1.5 Interface Requirements | --- | --- |  |
| 3.2.1.5.1 Reserved | --- | --- |  |
| 3.2.1.5.1.1 Reserved | --- | --- |  |
| 3.2.1.5.1.2 Reserved | --- | --- |  |
| 3.2.1.5.1.3 Reserved | --- | --- |  |
| 3.2.1.5.1.4 Interface with NAS Systems 1) | 1500 | D |  |
| 3.2.1.5.1.4 Interface with NAS Systems 2) | 1501 | D |  |
| 3.2.1.5.1.4 Interface with NAS Systems 3) | 1502 | D |  |
| 3.2.1.5.1.4 Interface with NAS Systems 4) | 1503 | D |  |
| 3.2.1.5.1.4 Interface with NAS Systems 5) | 1504 | D |  |
| 3.2.1.5.1.4 Interface with NAS Systems 6) | 1505 | D |  |
| 3.2.1.5.1.4 Interface with NAS Systems 7) | 1506 | D |  |
| 3.2.1.5.1.4.1 Reserved |  |  |  |
| 3.2.1.5.1.5 Automatic Call Detection | 485 | D |  |
| 3.2.1.5.1.5 Automatic Call Detection | 486 | D |  |
| 3.2.1.5.1.6 Call-Termination | 487 | D |  |
| 3.2.1.5.1.6 Call-Termination | 488 | D |  |
| 3.2.1.5.1.6 Call-Termination | 489 | D |  |
| 3.2.1.5.2 DUAT TCP/IP Interfaces | 491 | D |  |
| 3.2.1.5.2 DUAT TCP/IP Interfaces | 492 | D |  |
| 3.2.1.5.2 DUAT TCP/IP Interfaces | 493 | D |  |
| 3.2.1.5.2.1 NAS Messages | 496 | D |  |
| 3.2.1.5.2.1 NAS Messages | 497 | D |  |
| 3.2.1.5.2.1.1 Originator's Address | 498 | D |  |
| 3.2.1.5.2.1.2 Data Exchanges | 499 | D |  |
| 3.2.1.5.2.1.2 Data Exchanges | 500 | D |  |
| 3.2.1.5.2.1.2 Data Exchanges | 501 | D |  |
| 3.2.1.5.2.1.2 Data Exchanges | 502 | D |  |
| 3.2.1.5.2.1.2 Data Exchanges | 503 | D |  |
| 3.2.1.5.2.1.2 Data Exchanges | 504 | D |  |
| 3.2.1.6 Performance Requirements | 505 | T/A |  |
| 3.2.1.6 Performance Requirements | 506 | T/A |  |
| 3.2.1.6 Performance Requirements | 507 | T/A |  |
| 3.2.1.6 Performance Requirements | 508 | T/A |  |
| 3.2.1.6 Performance Requirements | 509 | T/A |  |
| 3.2.1.6 Performance Requirements | 510 | T/A |  |
| 3.2.1.6 Performance Requirements | 511 | T/A |  |
| 3.2.1.6 Performance Requirements | 512 | T/A |  |
| 3.2.1.6 Performance Requirements | 513 | T/A |  |
| 3.2.1.6 Performance Requirements | 514 | T/A |  |
| 3.2.1.6 Performance Requirements | 515 | T/A |  |
| 3.2.1.6 Performance Requirements | 516 | T/A |  |
| 3.2.1.6 Performance Requirements | 517 | T/A |  |
| 3.2.1.6 Performance Requirements | 518 | T/A |  |
| 3.2.1.6 Performance Requirements | 519 | T/A |  |
| 3.2.1.6 Performance Requirements | 520 | T/A |  |
| 3.2.1.6 Performance Requirements | 521 | T/A |  |
| 3.2.1.6 Performance Requirements | 522 | T/A |  |
| 3.2.1.6 Performance Requirements | 523 | T/A |  |
| 3.2.1.6.1 Simultaneous Users | 524 | D |  |
| 3.2.1.6.2 Time Source Synchronization | 525 | D |  |
| 3.2.1.6.3 Flight Plan Error Rate | 526 | A |  |
| 3.2.1.6.3 Flight Plan Error Rate | 527 | D |  |
| 3.2.1.6.3 Flight Plan Error Rate | 528 | D |  |
| 3.2.1.6.4 Qualified Internet Communications Provider (QICP) Requirement | 1507 | A |  |
| 3.2.1.6.4 Qualified Internet Communications Provider (QICP) Requirement | 1508 | A |  |
| 3.2.1.6.4 Qualified Internet Communications Provider (QICP) Requirement | 1509 | A |  |
| 3.2.2 Reserved | --- | --- |  |
| 3.2.3 System Quality Factors | --- | --- |  |
| 3.2.3.1 Reliability | 530 | A |  |
| 3.2.3.2 Maintainability | 531 | A |  |
| 3.2.3.3 Availability | 532 | A |  |
| 3.2.3.3 Availability | 073 | A |  |
| 3.2.3.3 Availability | 536 | D |  |
| 3.2.4 System Flexibility and Growth | 537 | A |  |
| 3.2.4.1 DUAT Service User Growth | 538 | A |  |
| 3.3 Reserved | --- | --- |  |
| 3.3.1 Human Engineering | 542 | D |  |
| 3.3.1.1 Human Factors | 543 | I |  |
| 3.3.1.1.1 Command Language | 544 | D |  |
| 3.3.1.1.2 User Feedback | 545 | D |  |
| 3.3.1.1.2.1 Feedback Message | 546 | D |  |
| 3.3.1.1.2.1 Feedback Message | 547 | D |  |
| 3.3.1.1.2.1.1 Feedback Time | 548 | D |  |
| 3.3.1.1.2.2 Error Messages | 549 | D |  |
| 3.3.1.1.2.2 Error Messages | 550 | D |  |
| 3.3.1.1.2.2.1 Command Response Message | 551 | D |  |
| 3.3.1.1.2.2.2 Command Error Message | 552 | D |  |
| 3.3.1.1.2.2.2 Command Error Message | 553 | D |  |
| 3.3.2 through 3.3.9 Reserved | --- | --- |  |
| 3.3.9.1 General Security Requirements | --- | --- |  |
| 3.3.9.1.1 Physical Security | 554 | I |  |
| 3.3.9.1.2 Telecommunications and Information Security | 555 | I |  |
| 3.3.9.1.3 User Passwords | 557 | I |  |
| 3.3.9.2 Access Levels | 558 | D |  |
| 3.3.9.2 Access Levels | 559 | D |  |
| 3.3.9.2 Access Levels | 560 | D |  |
| 3.3.9.2.1 Weather Briefing/Flight Planning Access | 561 | D |  |
| 3.3.9.2.1 Weather Briefing/Flight Planning Access | 562 | D |  |
| 3.3.9.2.2 Authorized Users Database Access | 563 | D |  |
| 3.3.9.2.2 Authorized Users Database Access | 564 | D |  |
| 3.3.9.2.3 User Information Display Area Access | 565 | D |  |
| 3.3.9.3 Reserved |  |  |  |
| 3.3.9.4 Access Restrictions | 566 | D |  |
| 3.3.9.5 Initial Access Validation | 567 | D |  |
| 3.3.9.5 Initial Access Validation | 568 | D |  |
| 3.3.9.5.1 Access Non-Validation | 569 | D |  |
| 3.3.9.5.1.1 New DUAT User Access | 570 | D |  |
| 3.3.9.5.1.1 1 Documentation Retention | 571 | D |  |
| 3.3.9.6 Access Code and Password Assignment | 572 | D |  |
| 3.3.9.6 Access Code and Password Assignment | 573 | D |  |
| 3.3.9.6.1 Access Codes | 574 | D |  |
| 3.3.9.6.1.1 Access Security | 575 | D |  |
| 3.3.9.6.1.2 Password | 576 | D |  |
| 3.3.9.6.1.2 Password | 577 | D |  |
| 3.3.9.6.2 Retention for Future Use | 578 | D |  |
| 3.3.9.7 Log-on | 579 | D |  |
| 3.3.9.7.1 Log-on Denial | 580 | D |  |
| 3.3.9.7.1 Log-on Denial | 581 | D |  |
| 3.3.9.7.1.1 Log-on Denial Remarks | 582 | D |  |
| 3.3.9.7.2 Record of Log-on Attempts | 583 | D |  |
| 3.3.9.8 Scope of the Information Systems Security Program | 1021 | D |  |
| 3.3.9.8 Scope of the Information Systems Security Program | 1022 | D |  |
| 3.3.9.8 Scope of the Information Systems Security Program | 1028 | D |  |
| 3.3.9.8.1 Security Implementation | 1033 | D |  |
| 3.3.9.8.2 Security Responsibilities | 1034 | D |  |
| 3.3.9.8.2 Security Responsibilities | 1035 | D |  |

# Text boxes

Figure 3.1-1

NAS

Interfaces

FTI

Gateway

Non-NAS

Interfaces

IP

NADIN MSN

Rehost

(NMR)

(NMR)

IP

IP

IP

FAA Data

National Flight Data Center Info

Airport Data

Airway Data

Facility Data

Weather Facility Data

NAVAIDs

Airmen’s Registry Data

Flight Publications

DUAT

Service Provider

Site

INTERNET

or

Phone Line

DUAT User