4910.1

APPENDIX K

24 CFR 200.926

Minimum Property Standards for Property which is not

Multifamily or Care-type Property

The following portions of 24 C.F.R. Part 200 have been

included for the convenience of the users of this handbook.  These

provisions establish procedures for the construction of one and two

family dwellings and reference standards found in the Appendices of

this handbook.

200.926  Minimum property standards for one- and two-family

dwellings.

(a)  Construction standards.

(1)  Applicable structures.  The standards identified or

contained in this section and  200.926 and 200.926a-200.926e

shall apply to single family detached homes,

duplexes, triplexes and to living units in a structure

where the units are located side-by-side in townhouse

fashion.

(2)  Applicability of standards to new construction.  The

standards referenced in paragraph (a)(1) of this section

are applicable to:

(i)  Structures approved for insurance or other benefits

prior to the start of construction, including

approval under the direct endorsement process

described in  203.5 of this chapter;

(ii) Structures which are approved for insurance or

other benefits based upon participation in an

insured warranty program;

(iii) Structures which are insured as new construction

based upon a Certificate of Reasonable Value issued

by the Veterans Administration.

K-1

1994

_____________________________________________________________________

4910.1

(b)  Conflicting standards.  The requirements contained in

200.926d do not preempt local or State standards, nor do they

alter or affect a builder's obligation to comply with any

local or State requirements.  However, a property shall be

eligible for benefits only if it complies with the

requirements of this subpart, including any referenced

standards.  When any of the requirements identified in

200.926c are in conflict with a partially accepted local or

State code, the conflict will be resolved by the HUD Field

Office servicing the jurisdiction in which the property is to

be located.

(c)  Standard for evaluating local or State building codes.  The

Secretary shall compare a local building code submitted under

200.926(d) or a State code to the list of construction

related areas contained in  200.926a.

(1)  A local or State code will be accepted if it regulates

each area and subarea on the list.  However, for seismic

design, ASCE 7-88, is mandatory.

(2)  A local or State building code will be partially accepted

if it regulates most of the areas on the list provided,

however, that no code may be partially accepted if it

fails to regulate subareas in more than one of the major

areas.  The major areas are:  fire safety, light and

ventilation, structural loads, foundation systems,

materials, standards, construction components, glass,

mechanical, plumbing and electrical.  See  200.926a.

(3)  For purposes of this paragraph, a local or State code

regulates an area or subarea if it establishes a standard

concerning that area or subarea.

(d)  Code selection.  Any materials required to be submitted under

this section must be submitted by the time the lender or other

interested party applies for mortgage insurance or other

benefits.

(1)  Jurisdictions without previously accepted building codes.

The following submission requirements apply to lenders

and other interested parties in jurisdictions without

building codes, jurisdictions with building codes which

previously have never been submitted for acceptance and

jurisdictions with building codes which previously have

been submitted for acceptance and have not been accepted

or partially accepted by the Secretary.

K-2

1994

_____________________________________________________________________

4910.1

(i)  In jurisdictions without local building codes:

(A)  If the State building code is acceptable, the

lender or other interested party must comply

with the State building code and the

requirements of  200.926d;

(B)  If the State building code is partially

acceptable, the lender or other interested

party must comply with:

(1)  The acceptable portions of the partially

acceptable code;

(2)  Those portions of the CABO One- and

Two-Family Dwelling Code or the Electrical

Code for One- and Two-Family Dwellings,

designated by the HUD Field Office, in

accordance with  200.926c; and

(3)  The requirements of  200.926d.

(C)  If there is no State building code or if the

State building code is unacceptable, the lender

or other interested party may comply with:

(1)  The CABO One- and Two-Family Code and the

Electrical Code for One-and Two-Family

Dwellings, as identified in  200.926b(a);

and

(2)  The requirements of  200.926d.

(ii) In jurisdictions with local building codes which

have never been submitted for review, lenders or

other interested parties must:

(A)  Comply with the requirements of

200.926(d)(1)(i)(A), (B) or (C), as

appropriate; or

(B)  Request the Secretary's acceptance of the

local building code in accordance with

200.926(d)(1)(iv).

K-3

1994

_____________________________________________________________________

4910.1

(1)  If the Secretary determines that the

local building code is unacceptable, then

the lender or other interested party must

comply with the requirements of  200.926

(d)(1)(i)(A), (B) or (C), as appropriate.

(2)  If the Secretary determines that the

local code is partially acceptable, then

the lender or other interested party must

comply with:

(i)  The acceptable portions of the

partially acceptable local code;

(ii)  Those portions of the CABO One- and

Two-Family Dwelling Code or

Electrical Code for One- and Two-Family

Dwellings designated by the

HUD Field Office in accordance with

200.926c;

(iii) The requirements of  200.926d; and

(3)  If the Secretary determines that the

local code is acceptable, then the lender

or other interested party must comply

with the local building code and the

requirements of  200.926d.

(iii)  In jurisdictions with local building codes which

previously have been submitted for review and which

have been found unacceptable by the Secretary:

(A)  If the local code has not been changed since

the date the code or changes thereto were

submitted to the Secretary, the lender or

other interested party must comply with the

requirements of  200.926(d)(1)(i)(A), (B) or

(C), as appropriate; or

(B)  If the local code has been changed since the

date when the code or changes thereto were

submitted to the Secretary, the lender or

other interested party must submit a copy of

all changes to the local building code,

including all applicable service codes and

K-4

1994

_____________________________________________________________________

4910.1

appendices  and a copy of the statute,

ordinance, regulation or order making such

changes in the code, which have been made

since the date when the code or other changes

thereto were last submitted to the Secretary.

However, the lender or other interested party

need not submit any part already in the

possession of the HUD Field Office.  Based

upon the Secretary's determination concerning

the acceptability of the local code as

changed, the lender or other interested party

must comply with the requirements of

200.926(d)(1)(ii)(B)(1), (2)  or (3), as

appropriate.

(iv)  In order to obtain the Department's approval of a

local code, the lender or other interested party

must submit the following material to the HUD Field

Office serving the jurisdiction in which the

property is to be constructed:

(A)  A copy of the jurisdiction's local building

code, including all applicable service codes

and appendices; and

(B)  A copy of the statute, ordinance, regulation,

or order establishing the code, if such

statute, ordinance, regulation or order is not

contained in the building code itself.

However, the lender or other interested party

need not submit any document already on file

in the HUD Field Office.

(2)  Jurisdictions with previously accepted or partially

accepted building codes.

(i)  The lender or other interested party shall submit

to the HUD Field Office serving the jurisdiction in

which the property is to be constructed:

(A)  A certificate stating that since the date when

the code or any changes thereto were last

submitted to the Secretary, the jurisdiction's

local building code has not been changed; or

K-5

1994

_____________________________________________________________________

4910.1

(B)  (1)  A copy of all changes to the

jurisdiction's building code, including

all applicable service codes, and

appendices, which have been made since

the date when the code or other changes

thereto were last submitted to the

Secretary.  However, the lender or other

interested party need not submit any part

already in the possession of the HUD

Field Office; and

(2)  A copy of the statute, ordinance

regulation, or order making such changes

in the code.

(ii) If, based upon changes to the local building code,

the Secretary determines that it is unacceptable,

the lender or other interested party must comply

with the requirements of  200.926(d)(1)(i)(A), (B)

or (C), as appropriate.

(iii) If the local building code was previously found by

the Secretary to be partially acceptable and there

have been no changes to it or if the local building

code was previously found by the Secretary to be

partially acceptable and if, based upon changes to

it, the Secretary determines that it is still

partially acceptable or if the local building code

was previously found by the Secretary to be

acceptable and if, based upon changes to it the

Secretary determines that it is partially

acceptable, then the lender or other interested

party must comply with  200.926(d)(1)(ii)(B),

(2)(i), (ii) and (iii).

(iv) If the local building code was previously found by

the Secretary to be partially acceptable and if,

based upon changes to it, the Secretary determines

that it is acceptable, or if the local building

code was previously found by the Secretary to be

acceptable and there have been no changes to the

code, or if the local building code was previously

found by the Secretary to be acceptable and if,

based upon changes to it, the Secretary determines

that it is still acceptable, then the lender or

other interested party must comply with the local

building code and the requirements of  200.926d.

K-6

1994

_____________________________________________________________________

4910.1

(3)  Notification of decision. The Secretary shall review the

material submitted under  200.926(d).  Following that

review, the Secretary shall issue a written notice

(except where there is a previously accepted or partially

accepted code which has not been changed) to the

submitting party stating whether local building code is

acceptable, partially acceptable or not acceptable.

Where the local building code is not acceptable, the

notice shall also state whether the State code is

acceptable, partially acceptable or not acceptable.

The notice shall also contain the basis for the

Secretary's decision and a notification of the submitting

party's right to present its views concerning the denial

of acceptance if the code is neither accepted nor

partially accepted.  The Secretary may, in his

discretion, permit either an oral or written presentation

of views.

(i)  Fire retardant treated plywood, where approved by a

State or local building code, shall not be

permitted for use in roof construction unless a HUD

technical suitability bulletin has been issued by

the Department for that product.

(ii) The Secretary shall review the material submitted

under 200.926(d).  Following that review, the

Secretary shall issue a written notice (except

where there is a previously accepted or partially

accepted code which has not been changed) to the

submitting party stating whether the local building

code is acceptable, partially acceptable or not

acceptable.  Where the local building code is not

acceptable, the notice shall also state whether the

State code is acceptable, partially acceptable or

not acceptable.  The notice shall also state the

basis for the Secretary's decision and a

notification of the submitting party's right to

present its views concerning the denial of

acceptance if the code is neither accepted nor

partially accepted.  The Secretary may, in his or

her discretion, permit either an oral or written

presentation of views.

K-7

1994

_____________________________________________________________________

4910.1

(4)  Department's responsibilities.

(i)  Each Field Office will maintain a current list of

jurisdictions with accepted local or State building

codes, a current list of jurisdictions with

partially accepted local or State building codes

which have not been accepted.  For local codes, the

lists will state the most recent date when the code

or changes thereto were submitted to the Secretary.

The lists, which shall be prepared by the Field

Offices, will be available to any interested party

upon request.  In addition, the list of

jurisdictions whose codes have been partially

accepted shall be identified in accordance with

200.926c those portions of the codes listed at

200.926b(a) with which the property must comply.

(ii) The Department is responsible for obtaining copies

of the State codes and any changes thereto.

200.926a  Residential building code comparison items.

HUD will review each local and State code submitted under this

subpart to determine whether it regulates all of the following

areas and subareas:

(a)  Fire safety.

(1)  Allowable height;

(2)  Fire separations;

(3)  Fire resistance requirements;

(4)  Egress doors and windows;

(5)  Unit smoke detectors;

(6)  Flame spread.

(b)  Light and ventilation.

(1)  Habitable rooms;

(2)  Bath and toilet rooms.

K-8

1994

_____________________________________________________________________

4910.1

(c)  Structural loads.

(1)  Design live loads;

(2)  Design dead loads;

(3)  Snow loads (for jurisdiction with snow loading conditions

identified in Section 7 of ASCE-7-88 (Formerly ANSI

A58.1)

(4)  Wind loads; Use ASCE-7-88

(5)  Earthquake loads (for jurisdictions in seismic zones 3 or

4 as identified in Section 9 of ASCE-7-88 (Formerly ANSI

A58.1)

(d)  Foundation systems.

(1)  Foundation depths;

(2)  Footings;

(3)  Foundation materials criteria.

(e)  Materials standards.

(1)  Materials standards.

(f)  Construction components.

(1)  Steel;

(2)  Masonry;

(3)  Concrete;

(4)  Lumber;

(5)  Roof construction and covering;

(6)  Chimneys and fireplaces.

(g)  Glass.

(1)  Thickness/area requirements;

(2)  Safety glazing.

(h)  Mechanical.

(1)  Heating, cooling and ventilation systems;

(2)  Gas, liquid and solid fuel piping and equipment;

(3)  Chimneys and vents;

(4)  Ventilation (air changes).

K-9

1994

_____________________________________________________________________

4910.1

(i)  Plumbing.

(1)  Materials standards;

(2)  Sizing and installing drainage systems;

(3)  Vents and venting;

(4)  Traps;

(5)  Cleanouts;

(6)  Plumbing fixtures;

(7)  Water supply and distribution;

(8)  Sewage disposal systems.

(j)  Electrical.

(1)  Branch circuits;

(2)  Services;

(3)  Grounding;

(4)  Wiring methods;

(5)  Cable;

(6)  Conduit;

(7)  Outlets, switches and junction boxes;

(8)  Panelboards.

200.926b  Model codes.

(a)  Incorporation by reference.  The following model code

publications are incorporated by reference in accordance with

5 U.S.C. 522(a) and 1 CFR Part 51.  The incorporation by

reference of these publications has been approved by the

Director of the Federal Register.  The locations where copies

of these publications are available are set forth below.

(1)  CABO One and Two Family Dwelling Code, 1992 Edition

including the 1993 amendments but excluding Chapter I

- Administration, and the phrase "or fire retardant wood"

contained in the exception of paragraph R-218.2.2(2) but

including the Appendices A, B, D, and E of the code.

(Available from the Council of American Building

Officials, Suite 708, 5203 Leesburg Pike, Falls Church,

VA 22041.)

(2)  Electrical Code for One and Two Family Dwellings, NFPA

70A, 1990 Edition, including appendices.  Available from

the National Fire Protection Association, Batterymarch

Park, Quincy, MA 02269.

K-10

1994

_____________________________________________________________________

4910.1

(b)  Model code compliance requirements.

(1)  When a one or two family dwelling is to comply with the

model codes set forth in  200.926(a), the following

requirements of those model codes shall not apply to

those properties:

(i)  Those provisions of the model codes that require or

allow the issuance of permits of any sort.

(2)  Where the model codes set forth in  200.926b(a) designate

a building, fire, mechanical, plumbing or other official,

the Secretary's designee in the HUD Field Office serving

the jurisdiction in which the dwelling is to be

constructed shall act as such officials.

(c)  Designation of Model Codes.  When a one or two family dwelling

or townhouse is to comply with portions of the model code or

the entire code, the dwelling shall comply with the CABO One

and Two Family Dwellings Code 1992 Edition, including the 1993

amendments but excluding Chapter I - Administration, or

portions thereof as modified by  200.926d(e) of this part and

designated by the HUD Field Office serving a jurisdiction in

which the property is located.  In addition, the property

shall comply with all the standards which are referenced for

any designated portions of the model code, and with the

Electrical Code for One and Two Family Dwellings, NFPA 70A,

1990.

(1)  CABO One and Two Family Dwelling Code, 1992 Edition with

the 1993 amendments.

(2)  Electrical Code for One and Two Family Dwellings, NFPA

70A, 1990.

200.926C  Model code provisions for use in partially accepted

code jurisdictions.

If a lender or other interested party is notified that a State

or local building code has been partially accepted, then the

properties eligible for HUD benefits in that jurisdiction shall be

constructed in accordance with the applicable State or local

building code, plus those additional requirements identified below.

Depending upon the major area identified in  200.926a which is not

adequately regulated by the State or local code, the HUD Field

Office will designate, in accordance with the schedule below, those

portions of one of the model codes with which the property must

comply.

K-11

1994

_____________________________________________________________________

4910.1

Schedule for Model Code Supplements to

Local or State Codes

_____________________________________________________________________

Deficient major from          Portions of the CABO One and

200.926a as determined by      Two Family Dwelling Code, 1992

Field Office review           Edition including the 1993

amendments with which a

property must comply and

Electrical code for One and

Two Family Dwellings

(NFPA 70A-1990)

_____________________________________________________________________

(a)  Fire safety.................. Chapters 2, 9,; Section R-402.

(b)  Light and ventilation........ Chapter 2; Section R-309.

(c)  Structural loads............. Chapter 2.

(d)  Foundation systems........... Chapter 3.

(e)  Materials standards.......... Chapter 26.

(f)  Construction components...... Part III.

(g)  Glass........................ Chapter 2.

(h)  Mechanical................... Part IV.

(i)  Plumbing..................... Part V.

(j)  Electrical................... Electrical Code for One and

Two Family Dwellings

(NFPA 70A-1990)

_____________________________________________________________________

200.926d  Construction Requirements

(a)  Application.

(1)  General.

These standards cover the agency requirements for

accessibility to physically disabled people, variations

to standards, real estate entity, trespass and utilities,

site conditions, access, site design, streets, dedication

of utilities, drainage and flood hazard exposure, special

construction and product acceptance, thermal

requirements, and water supply systems.

K-12

1994

_____________________________________________________________________

4910.1

(2)  Requirements for Accessibility to Physically Disabled

People

The HUD Field Office will advise project sponsors as to

the extent accessibility will be required for new

construction of one- and two-family dwellings on a

project-by-project basis.

(i)  Technical Standards

See HUD, Minimum Property Standards, 4910.1 See 24

CFR Part 40.

(3)  Variations to standards.

(i)  New materials and technologies.

See  200.926d(d).  Alternatives, nonconventional

or innovative methods and materials shall be

equivalent to these standards in the areas of

structural soundness, durability, economy of

maintenance or operation and usability.

(ii)  Variation procedures.

Variations from the requirements of any standard

with which the Department requires compliance shall

be made in the following ways:

(A)  For a particular design or construction method

to be used on a single case or project, the

decision is the responsibility of the Field

Office.  Headquarters concurrence is not

required.

(B)  Where a variation is intended to be on a

repetitive basis, a recommendation for a Local

Acceptable Standard, substantiating data, and

background information shall be submitted by

the Field Office to the Director, Office of

Manufactured Housing and Regulatory Functions.

(iii) Variances which require individual analysis and

decision in each instance are not considered as

repetitive variances even though one particular

standard is repeatedly the subject of variation.

Such variances are covered by  200.926d(a)(3)(ii)(A).

K-13

1994

_____________________________________________________________________

4910.1

(b)  General acceptability criteria.

(1)  Real estate entity.

The property shall comprise a single plot except

that a primary plot with a secondary plot for an

appurtenant garage or for other use contributing to

the marketability of the property will be

acceptable provided the two plots are in such

proximity as to comprise a readily marketable real

estate entity.

(2)  Service and facilities.

(i)  Trespass.

Each living unit shall be one that can be used

and maintained individually without trespass

upon adjoining properties, except when the

windowless wall of a detached dwelling is

located on a side lot line.  A detached

dwelling may be located on a side lot line if:

(A)  Legal provision is made for permanent

access for the maintenance of the

exterior portion of the lot line wall,

and

(B)  The minimum distances from the dwelling

to the dwellings on the abutting

properties are not less than the sum of

the side yard distances computed as

appropriate for the type of opposing

walls.  (Minimum distance 10 ft.)

(ii)  Utilities.

Utility services shall be independent for each

living unit, except that common services such

as water, sewer, gas and electricity may be

provided for living units under a single

mortgage or ownership.  Separate utility

service shut-off for each unit shall be

provided.  For living units under separate

ownership, common utility services may be

provided from the main to the building line

when protected by an easement or convenant and

maintenance agreement acceptable to HUD, but

K-14

1994

_____________________________________________________________________

4910.1

shall not pass over, under or through any

other living unit.  Individual utilities

serving a living unit may not pass over, under

or through another living unit under the same

mortgage unless provision is made for repair

and maintenance of utilities without trespass

or when protected by an easement of covenant

providing permanent access for maintenance and

repair of the utilities.  Building drain

cleanouts shall be accessible from the

exterior where a single drain line within the

building serves more than one unit.

(3)  Site conditions.

(i)  The property shall be free of those

foreseeable hazards and adverse conditions

which may affect the health and safety of the

occupants or the structural soundness of the

improvements, or which may impair the

customary use and enjoyment of the property.

The hazards include toxic chemicals,

radioactive materials, other pollution,

hazardous activities, potential damage from

soil or other differential ground movements,

ground water, inadequate surface drainage,

flood, erosion, or other hazards located on or

off site.  The site must meet the standards

set forth at 24 CFR Part 51, and HUD Handbook

4910.1, Section 606 for termite and decay

protection.

(ii) When special conditions exist or arise during

construction which were unforeseen and which

necessitate precautionary or hazard mitigation

measures, the HUD Field Offices shall require

corrective work to mitigate potential adverse

effects from the special conditions as may be

necessary.  Special conditions include rock

formations, unstable soils or slopes, high

ground water level, springs, or other

conditions which may adversely effect a

property.  It shall be the builder's

responsibility to assure proper design,

construction and satisfactory performance

where they are present.

K-15

1994

_____________________________________________________________________

4910.1

(4)  Access.

(i)  Each property shall be provided with vehicular

or pedestrian access by public or private

streets.  Private streets shall be protected

by permanent easement.

(ii)  Each living unit shall have a means of access

such that it is unnecessary to pass through

any other living unit.

(iii) The rear yard shall be accessible without

passing through any other living unit.

(iv)  For a row type dwelling, the access may be by

means of alley, easement, passage through the

dwelling, or other means acceptable to the HUD

Field Office.

(c)  Site design.

(1)  General.

(i)  A site design shall be provided which includes

an arrangement of all site facilities

necessary to create a safe, functional,

healthful, durable and energy efficient living

environment.

(ii)  These site design standards are applicable

only in communities which have not adopted

criteria for site development applicable to

one and two family dwellings.

(iii) Single family detached houses situated on

individual lots located on existing streets

with utilities need not comply with the

requirements of  200.926d(c)(2), (3) and

(4)(ii).

(2)  Streets.

(i)  Existing or proposed streets on the site shall

connect to private or public street and shall

provide all-weather access to all building for

essential and emergency use, including access

for deliveries, service, maintenance and fire

equipment.

K-16

1994

_____________________________________________________________________

4910.1

(ii)  Streets shall be designed for dedication for

public use and maintenance or, when approved

by the HUD Field Office, may be retained as

private streets where protected by permanent

easements.

(3)  Dedication.

Utilities shall be located to permit dedication to

the local government or appropriate public body.

(4)  Drainage and flood hazard exposure.

(i)  Residential structures with basements located

in FEMA-designated areas of special flood

hazard.  The elevation of the lowest floor in

structures with basements shall be at or above

the base flood level (100 year flood level)

required for new construction or substantial

improvement of residential structures under

regulations for the National Flood Insurance

Program (NFIP) (see 44 CFR 60.3 through 60.6),

except where variances from this standard are

granted by communities under the procedures of

the Federal Emergency Management Agency (FEMA)

at 44 CFR 60.6(a) or exceptions from this NFIP

standard for basements are approved by FEMA in

accordance with procedures at 44 CFR 60.6(c).

(ii) Residential structures without basements

located in FEMA-designated areas of special

flood hazard.  The elevation of the lowest

floor in structures without basements shall be

at or above the FEMA-designated base flood

elevation (100 year flood level).

(iii) Residential structures located in

FEMA-designated "coastal high hazard areas".  (A)

Basements or any permanent enclosure of space

below the lowest floor of a structure are

prohibited.

(B)  Where FEMA has determined the base flood

level without establishing stillwater

elevations, the bottom of the lowest

structural member of the lowest floor

(excluding pilings and columns) and its

horizontal supports shall be at or above the

base flood level.

K-17

1994

_____________________________________________________________________

4910.1

(iv) "Critical Actions" as defined in 24 CFR

55.2(b)(2).  The lowest floor of a structure

(including the basement and all mechanical,

electrical, and service equipment) shall be at

or above the FEMA-designated 500 year

frequency flood elevation.  "Critical Actions"

located in FEMA-designated "floodways" (as

defined in 24 CFR 55.2(b)(4)) and "coastal

high hazard areas" (as defined in 24 CFR 55.2

(b)(1)) are prohibited.

(v)  Streets.  Streets must be usable during runoff

equivalent to a 10 year return frequency.

Where drainage outfall is inadequate to

prevent runoff equivalent to a 10 year return

frequency from ponding over 6 inches deep,

streets must be made passable for commonly

used emergency vehicles during runoff

equivalent to a 25 year return frequency

except where as alternative access street not

subject to such ponding is available.

(vi) Crawl spaces.  Crawl spaces must not pond

water or be subject to prolonged dampness.

(d)  Special construction and product acceptance.

(1)  Structural features of factory produced (modular or

panelized) housing or components.

(i)  For factory fabricated systems or components,

HUD Handbook 4950.1, "Technical Suitability of

Products Program Processing Procedures" shall

apply.

(ii) The requirements of this Part shall apply to

structural features, consisting of factory

fabricated systems or components assembled

either at the factory or at the construction

site, if the total construction is covered by

these standards and can be inspected on-site

for determination of compliance.

K-18

1994

_____________________________________________________________________

4910.1

(2)  Non-structural or non-standard features.

These features include methods of construction,

systems, sub-systems, components, materials and

processes which are not covered by these

requirements.  See HUD Handbook 4950.1 for

procedures to be followed in order to obtain

acceptance of non-structural components or

materials.  See HUD Handbook 4910.1 Appendix F for

a list of Use of Materials Bulletins.  Products and

methods shall conform to the appropriate Use of

Materials Bulletin.

(3)  Standard features.

These features include methods of construction,

systems, sub-systems, components, materials and

processes which are covered by national society or

industry standards.  For a list of standards to

which compliance is required, see HUD Handbook

4910.1, Appendices C, E and F.

(e)  Energy efficiency

All detached One and Two Family Dwellings and One Family

Townhouses not more than three stories in height shall

comply with the CABO Model Energy Code, 1992 Edition,

Residential Buildings, except for Sections 101.3.1,

101.3.2, 104 and 105, but Section 101.3.2.2, Historic

Buildings, shall remain, and including the Appendix, and

HUD intermediate MPS Supplement 4930.2 Solar Heating and

Domestic Hot Water Systems, 1989 edition.

(f)  Water supply systems.

(1)  General.

(i)  Each living unit shall be provided with a

continuing and sufficient supply of safe water

under adequate pressure and of appropriate

quality for all household uses.  Newly

constructed residential property for which a

building permit has been applied for on or

after June 19, 1988 from the competent

authority with jurisdiction in this matter

shall have lead-free water piping.  For

K-19

1994

_____________________________________________________________________

4910.1

purposes of these standards, water piping is

"lead-free" if it uses solders and flux

containing not more than 0.2 percent lead and

pipes and pipe fittings containing not more

than 8.0 percent lead.  This system shall not

impair the function or durability of the

plumbing system or attachments.

(ii) The chemical and bacteriological standards of

the local health authority shall apply.  In

the absence of such standards, the maximum

contaminant levels of EPA shall apply.  A

water analysis may be required by either the

health authority or the HUD Field Office.

(iii) Whenever feasible, connection shall be made to

a public water system.  When a public system

is not available, connection shall be made to

a community system which shall comply with HUD

Handbook 4940.2.

(2)  Individual Water Systems.

(i)  The system should be capable of delivering a

flow of 5 gpm over at least a 4 hour period.

(ii)  Water that, to be potable, requires continuing

or repetitive treatment to be safe bacterially

or chemically shall also comply with the

requirements of 24 CFR 203.52 or 24 CFR

234.64, whichever is applicable.

(iii) After installation, the system shall be

disinfected in accordance with the

recommendations or requirements of the local

health authority.  In the absence of a health

authority, system cleaning and disinfection

shall conform to the current EPA Manual of

Individual Water Supply Systems.

(iv)  Bacteriological or chemical examination of a

water sample collected by a representative of

the local or state health authority shall be

made when required by that authority or the

HUD Field Office.

K-20

1994

_____________________________________________________________________

4910.1

(3)  Location of wells.

(i)  A well located within the foundation walls of

a dwelling is not acceptable except in arctic

or subarctic regions.

(ii) Water which comes from any soil formation

which may be polluted, contaminated, fissured,

creviced or less than 20 ft. below the natural

ground surface is not acceptable, unless

acceptable to the local health authority.

(iii) Individual water supply systems are not

acceptable for individual lots in areas where

chemical soil poisoning has been or is

practiced if the overburden of soil between

the ground surface and the water bearing

strata is coarse grained sand, gravel, or

porous rock, or is creviced in a manner which

will permit the recharge water to carry the

toxicants into the zone of saturation.

(iv)  The following table shall be used in

establishing the minimum acceptable distances

between wells and sources of pollution located

on either the same or adjoining lots.  These

distances may be increased by either the

health authority having jurisdiction or the

HUD Field Office.

K-21

1994

_____________________________________________________________________

4910.1

DISTANCE FROM SOURCE OF POLLUTION

_________________________________________________________________

Minimum  Horizontal

Source of Pollution               Distance (ft.)

_________________________________________________________________

Property Line                           10

Septic Tank                             50

Absorption Field                       100/1

Seepage Pit                            100/1

Absorption Bed                         100/1

Sewer Lines

w/Permanent Watertight Joints          10

Other Sewer Lines                       50

Chemically Poisoned Soil                25/3

Dry Well                                50

Other                                  ___/2

_________________________________________________________________

Note:

1    This clearance may be increased or decreased depending

upon soil and rock penetrated by the well and aquifer

conditions.  The clearance may be increased in creviced

limestone and permeable strata of gravel and sand.  The

clearance may be reduced to 50 ft. only where the ground

surface is effectively separated from the water bearing

formation by an extensive, continuous impervious strata

of clay, hardpan, or rock.  The well shall be constructed

so as to prevent the entrance of surface water and

contaminants.

2    The recommendations or requirements of the local health

authority shall apply.

3    This clearance may be reduced to 15 feet only where the

ground surface is effectively separated from the water

bearing formation by an extensive, continuous impervious

strata of clay, hardpan, or rock.

(4)  Well Construction

(i)  The well shall be constructed so as to allow

the pump to be easily placed and to function

properly.

(ii) (A)  All drilled wells shall be provided with

a sound, durable and watertight casing

capable of sustaining the loads imposed.

K-22

1994

_____________________________________________________________________

4910.1

(B)  The casing shall extend from a point

several feet below the water level at

drawdown or from an impervious strata

above the water level to 12 in. above

either the ground surface of the pump

room floor.  The casing shall be sealed

at the upper opening to a depth of at

least 15 feet.

(iii)     Bored wells shall be lined with concrete,

vitrified clay or equivalent materials.

(iv)      The space between the casing or liner and

the wall of the well hole shall be sealed

with cement grout.

(v)       The well casing shall not be used to

convey water except under positive

pressure.  A separate drop pipe shall be

used for the suction line.

(vi)      When sand or silt is encountered in the

water-bearing formation, the well shall

either be compacted and gravel packed, or

a removable strainer or screen shall be

installed.

(vii)     The surface of the ground above and

around the well shall be compacted and

graded to drain surface water away from

the well.

(viii)    Openings in the casing, cap, or concrete

cover for the entrance of pipes, pumps or

manholes shall be water tight.

(ix)      If a breather is provided, it shall

extend above the highest level to

which surface water may rise.  The

breather shall be watertight, and

the open end shall be screened and

positioned to prevent entry of dust,

insects, and foreign objects.

K-23

1994

_____________________________________________________________________

4910.1

(5)  Pump and equipment.

(i)  Pumps shall be capable of delivering the

volume of water required under normal

operating pressure within the living unit.

Pump capacity shall not exceed the output of

the well.

(ii)  Pumps and equipment shall be mounted to be

free of objectionable noises, vibrations,

flooding, pollution, and freezing.

(iii) The suction line shall terminate below the

maximum drawdown of the water level in the

well.

(iv)  Horizontal segments of suction line shall be

placed below the frost line in a sealed casing

pipe or in at least 4 in. of concrete.  The

distance from suction lines to sources of

pollution shall be not less than shown in the

table at  200.926d(f)(3)(iv) of this section.

(6)  Storage tanks.

(i)  A pressure tank having a minimum capacity of

42 gallons shall be provided.  However,

prepressured tanks and other pressurizing

devices are acceptable provided that delivery

between pump cycles equals or exceeds that of

a 42 gallon tank.

(ii) Tanks shall be equipped with a clean-out plug

at the lowest point, and a suitable pressure

relief valve.

200.926e  Supplemental information for use with the CABO One and

Two Family Dwelling Code.

The following shall be used in Table No. R-201.2, Climatic and

Geographic Design Criteria of the CABO One and Two Family Dwelling

Code.

(a)  Roof live loads.

Roof slope 3 in 12 or less:  20 psf

Roof slope over 3 in 12:  15 psf

Roof used as deck:  40 psf

K-24

1994

_____________________________________________________________________

4910.1

(b)  Roof snow load.  The roof snow load shall be in accordance

with Section 7 of ASCE 7-88 (Formerly ANSI A58.1).

(c)  Wind pressures.  The minimum Design Wind Pressures (net

pressures)  set forth below apply to areas designated as

experiencing basic wind speeds up to and including 80 mph, as

shown in ASCE 7-88, Figure 1, Basic Wind Speed Map.  These

pressures also apply to buildings not over 30 ft. in height

above finish grade, assuming exposure C or defined in ASCE 7-88

(Formerly ANSI A58.1).

(1)  Minimum design wind pressure criteria.

(i)  Buildings (for overturning, racking or

sliding); p = 20 psf.

(ii) Chimneys, p = 30 psf.

(iii) Exterior walls, p = 15 psf inward or outward.

Local pressure at corners of walls shall be

not less than p = 30 psf outward.  These local

pressures shall not be included with the

design pressure when computing overall loads.

The pressures shall be applied perpendicularly

outward on strips of width equal to 10 percent

of the least width of building.

(iv) Partitions, p = 10 psf.

(v)  Windows, p = 20 psf inward or outward.

(vi) Roof, p = 20 psf inward or outward.

Roofs with slopes greater than 6 in 12 shall be designed

to withstand pressures acting inward normal to the

surface, equal to the design wind pressure for exterior

walls.  Overhanging eaves, cornices, and ridges, 40 psf

upward normal to roof surface.  These local pressures

shall not be included with the design pressure when

computing overall loads.  The pressures shall be applied

perpendicularly outward on strips of width equal to 10

percent of the least width of building.  Net uplift on

horizontal projection or roof shall not be less than 12

psf.

K-25

1994

_____________________________________________________________________

4910.1

(2)  Severe wind design pressures.  If the construction is

higher than 30 ft., or if it is located in an area

experiencing wind speeds greater than 80 mph, higher

design wind pressures than shown above are required.  Use

Section 6 of ASCE 7-88 for higher criteria and for

determining where wind speeds greater than 80 mph occur.

Pressures are assumed to act horizontally on the gross

area of the vertical projection of the structure except

as noted for roof design.

(d)  Seismic conditions shall be in accordance with Section 9 of

ASCE 7-88 (Formerly ANSI A 58.1-82).

(e)  Subject to damage from:  weathering.  A jurisdiction's

weathering region shall be as established by the map in ASTM

C 62-88.

(f)  Subject to damage from:  frost line depth.  Exterior wall

footings or foundation walls including those of accessory

buildings shall extend a minimum of 6 in. below the finished

grade and, where applicable, the prevailing frost line.

(g)  Subject to damage from:  termites.  "Yes" shall be used in

locations designated as Very Heavy, Moderate to Heavy and

Slight to Moderate.  "No." shall be used in locations

designated as None to Slight.  The map for Termite Infestation

Probability in Appendix A of CABO, One and Two Family Dwelling

Code shall be used to determine the jurisdiction's region.

(h)  Subject to damage from:  decay.  "Yes" shall be used in

locations designated as moderate to severe and slight to

moderate.  "No." shall be used in locations designated as none

to slight.  The Decay Probability map in Appendix A of CABO,

One and Two Family Dwelling Code shall be used to determine

the jurisdiction's decay designation.

K-26

1994