# CONSTRUCTED WETLAND

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 656

### CONSTRUCTED WETLAND

A constructed wetland is an artificial ecosystem consisting of a shallow basin established with hydrophytic vegetation that is constructed to intersect and treat the flow of a waste stream or contaminated runoff.

### PRACTICE INFORMATION

Constructed wetlands are used to treat wastewater and contaminated runoff from agricultural processing, livestock, and aquaculture facilities or for improving the quality of storm water or other water flows lacking specific water quality discharge criteria.

For the constructed wetland to work properly, inlet control is provided to prevent debris from entering the wetland, and outlet control is provided to maintain appropriate water depths for wetland vegetation and the design hydraulic retention time.

The constructing wetland is a discharging practice, and therefore, the discharge must either be captured elsewhere in the wastewater treatment
system or discharged to the ecosystem in a manner consistent with discharge permit requirements.

Wetland plants are established that are suitable for local climatic conditions and tolerant of the contaminated flow the wetland is designed to attenuate. Invasive of nonnative species that could become a problem in the native habitat are not used.

### COMMON ASSOCIATED PRACTICES

A constructed wetland is commonly planned as part of a Conservation Management System with Waste Storage Facility (313), Waste Utilization (633), Critical Area Planting (342), Nutrient Management (590), Solid/Liquid Separation Facility (632), and other conservation practices.

For further information, refer to the practice standard in the local Field Office Technical Guide and associated job sheets.

# Text boxes

I.16 (+) Plant productivity

I.8 (+) Dissolved contaminants to ground water

Associated practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

I.3 (-) Potential income

I.14 (+) Methane in atmosphere

I.9 (-) Ground water quality

I.1 (+/-) Net return to producer

D.4 (+) Wetland habitat

I.15 (+) Greenhouse gases

C.5 (+/-) Air quality

D.2 (+) Impounded water

D.3 (+) Capture and transformation of pollutants by vegetation and microorganisms

Waste Storage Facility (313)

I.12 (+) Landscape diversity

C.1 (+/-) Income and income stability (individuals and community)

Note: Effects are qualified with a plus (+) or minus
(-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

D.1 (+) Cost of installation and maintenance

2. Hydrophytic vegetation

Constructed Wetland

6/2008

Start

C.2 (+/-) Quality of receiving waters

I.5 (+) Evaporation

Initial setting: A system where interception and treatment of one of the following is needed: (1) effluent from a manure management facility, or (2) contaminated storm water runoff

Constructed Wetland (656)

C.4 (+/-) Biodiversity

I.11 (-) Cost of compliance with future regulations

I.18 (+) Carbon sequestration

I.4 (+) Temporary flood storage

LEGEND

1. Shallow basin

3. Wastewater interception system

I.10 (+) Surface water quality

(-) dissolved contaminants

(-) particulate contaminants

(-) turbidity

(-) water-borne pathogens

C.3 (+/-) Community health and well being

I.17 (+) Oxygen production

I.13 (+) Wildlife habitat and diversity

I.2 (-) Available land for other uses

I.6 (+) Seepage

I.7 (-) Runoff