NASA

Capability Road Map (CRM) 12

Science Instruments and Sensors

Capability Portfolio

Chair:  Richard Barney, NASA GSFC

Co-Chair:  Maria Zuber, MIT

Deputy Chair:  Juan Rivera, NASA GSFC

Coordinators

Directorate	APIO

Harley Thronson, NASA SMD	Perry Bankston, NASA JPL

Giulio Varsi, NASA SMD

Team Members

NASA / JPL	Academia

Brian Ramsey, NASA MSFC	Chris Ruf, University of Michigan

Bruce Spiering, NASA SSC	Steve Ackerman, University of Wisconsin

Soren Madsen, NASA JPL	Suzanne Staggs, Princeton

Craig McCreight, NASA ARC

Tim Krabach, NASA JPL	Industry

Azita Valinia, NASA GSFC	Ron Polidan, Northrop Grumman

Paul Mahaffy, NASA GSFC	Rich Dissly, Ball Aerospace

David Chenette, Lockheed Martin

Consultants

David Glackin, Aerospce Corp.	Technical Experts

Richard McEntire, JHU/APL	Carl Stahle, NASA GSFC

Shyam Bajpai, NOAA	Amy Walton, NASA ESTO

Lee Rickard, Naval Research Laboratory	Louis Barbier, NASA GSFC

Thomas Black, NRO

TABLE OF CONTENTS

12.1	General Portfolio Overview	1

12.1.1	Technology Capability Description	1

12.1.2 	Benefits and Traceability	1

12.1.2.1	Enabled Missions/Science Goals	1

12.1.2.2	Traceability to Vision and Other Priority Agency Objectives	2

12.1.3 	Assumptions, Qualifications, Provisions and Legacy Activities	2

12.1.4 	Key Architecture/Strategic Decisions	3

12.1.5 	Major Technical Challenges	4

12.1.6 	Key Capabilities and Status	5

12.2	Detailed Portfolio Discussions	8

12.2.1	Microwave Instruments and Sensors	8

12.2.1.1 	Summary Description of Major Component Technologies	8

12.2.1.2 	Benefits and Relationship to Missions and to Strategies	8

12.2.1.3 	Metrics and Major Requirements	9

12.2.1.4 	Current State of the Art/Practice; Timeframe for Deployment	10

12.2.1.5 	Demonstration and Precursor Mission(s)	13

12.2.2 	Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR)	13

12.2.2.1 	Summary Description of Major Component Technologies	13

12.2.2.2 	Benefits and Relationship to Missions and to Strategies	14

12.2.2.3 	Metrics and Major Requirements	14

12.2.2.4 	Current State-of-the-Art/Practice; Timeframe for Deployment	15

12.2.2.5 	Demonstration and Precursor Mission(s)	19

12.2.3 	Multi-Spectral Sensing (UV-Gamma)	19

12.2.3.1 	Summary Description of Major Component Technologies	19

12.2.3.2 	Benefits and Relationship to Missions and to Strategies	20

12.2.3.3 	Metrics and Major Requirements	20

12.2.3.4 	Current State-of-the-Art/Practice; Timeframe for Deployment	21

12.2.3.5 	Demonstration and Precursor Mission(s)	25

12.2.4 	Laser/LIDAR Remote Sensing	25

12.2.4.1 	Summary Description of Major Component Technologies	25

12.2.4.2 	Benefits and Relationship to Missions and to Strategies	26

12.2.4.3 	Metrics and Major Requirements	26

12.2.4.4 	Current State-of-the-Art/Practice; Timeframe for Deployment	27

12.2.4.5 	Demonstration and Precursor Mission(s)	31

12.2.5 	Direct Sensing of Particles, Fields and Waves	31

12.2.5.1 	Summary Description of Major Component Technologies	31

12.2.5.2 	Benefits and Relationship to Missions and to Strategies	32

12.2.5.3 	Metrics and Major Requirements	34

12.2.5.4 	Current State-of-the-Aart/Practice; Timeframe for Deployment	34

12.2.5.5 	Demonstration and Precursor Mission(s)	38

12.2.6 	In Situ Instrumentation	38

12.2.6.1 	Summary Description of Major Component Technologies	38

12.2.6.2 	Benefits and Relationship to Missions and to Strategies	39

12.2.6.3 	Metrics and major requirements	39

12.2.6.4 	Current State-of-the-Art/Practice; Timeframe for Deployment	40

12.2.6.5 	Demonstration and Precursor Mission(s)	44

12.3	Roadmap Process		44

12.3.1 	Summary History of Roadmap Team, Meetings and Presentations	44

12.3.2 	Capability Breakdown Structure (CBS)	45

12.3.3 	Connection to Other Roadmaps	46

12.4.1 	Major Conclusions and Recommendations	48

12.4.2 	Next Steps		52

12.5	Acknowledgement/References	52

12.5.1 	Acknowledgement	52

12.5.2 	References		52

12.5.2.1 	Strategic Documents	52

12.5.2.2 	National Research Council Reports	53

12.5.2.3 	APIO Design Reference Missions	53

12.5.2.4 	Advanced Mission Studies: Mars Exploration Program

Analysis Group	53

12.5.2.5 	Enterprise Strategies	54

12.A	Appendices		A-1

12.A.1 	Design Reference Mission Set	A-1

12.A.2 	Science Traceability Matrix	A-2

12.A.3 	Sub-Capability Team Expertise	A-5

12.A.4 	Detailed Assumptions of the Roadmapping Process	A-7

12.A.4.1 	Scope	A-7

12.A.4.2 	SIS Library	A-7

12.A.4.3 	Science Traceability Spreadsheets	A-7

12.A.4.4 	References from the Master Spreadsheets	A-9

12.A.4.5 	Roadmap Development Overall Process	A-9

12.A.4.6 	SIS Top-Level Assumptions	A-11

12.A.4.7 	Microwave Instruments and Sensors (12.1) Assumptions	A-12

12.A.4.8 	Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR) (12.2)

Assumptions	A-12

12.A.4.9 	Multi-Spectral Sensing (UV-Gamma) (12.3) Assumptions	A-13

12.A.4.10 	Laser/LIDAR Remote Sensing (12.4) Assumptions	A-14

12.A.4.11 	Direct Sensing of Particles, Fields and Waves (12.5)

Assumptions	A-14

12.A.4.12 	In Situ Instrumentation (12.6) Assumptions	A-15

12.A.5	Acronyms and Abbreviations	A-17

TABLES

12.1.1	Impacts of Key Architectural and Strategic Decisions		4
12.1.2	Major Technical Challenges		5
12.1.3	Status of Key Capabilities		6
12.2.1	Metrics for Microwave Instrumentation		9
12.2.2	Current State of Practice for Microwave Instrumentation		10
12.2.3	Metrics for Vis-IR-FIR Imaging and Spectroscopic Instrumentation		15
12.2.4	Current State of Practice for Vis-IR-FIR Imaging and Spectroscopic

Instrumentation		16
12.2.5	Metrics for UV-Gamma Ray Imaging and Spectrometric Instrumentation		21
12.2.6	Current State of Practice for UV-Gamma Ray Imaging and Spectrometric

Instrumentation		22
12.2.7	Metrics for Laser/LIDAR Remote Sensing Instrumentation		27
12.2.8	Current State of Practice of Laser/LIDAR Remote Sensing Instrumentation		28
12.2.9	Metrics for Direct Sensing Instrumentation		33
12.2.10	Current State of Practice of Direct Sensing Instrumentation		34
12.2.11	Metrics for In Situ Instrumentation		39
12.2.12	Current State of Practice for In Situ Instrumentation		40
12.3.1	Interrelationships to Other Capability and Strategic Roadmaps		46
12.4.1	Key Sub-Capabilities		47
12.4.2	Critical Facility Needs		49
12.4.3	“Breakthrough” Technologies for Future Mission Architectures		50

12.A.1	Missions Referenced in Roadmaps		A-1

12.A.2	Sample Excerpt from Science Traceability Database	A-3

FIGURES

12.1a	Microwave Instruments and Sensors Near Term Capability Roadmap		11
12.1b	Microwave Instruments and Sensors Far Term Capability Roadmap		12
12.2a	Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR) Near Term

Capability Roadmap		17
12.2b	Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR) Far Term

Capability Roadmap		18
12.3a	Multi-Spectral Sensing (UV-Gamma) Near Term Capability Roadmap		23
12.3b	Multi-Spectral Sensing (UV-Gamma) Far Term Capability Roadmap		24
12.4a	Laser/LIDAR Remote Sensing Near Term Capability Roadmap		29
12.4b	Laser/LIDAR Remote Sensing Near Far Capability Roadmap		30
12.5a	Direct Sensing of Particles, Fields and Waves Near Term Capability Roadmap		35
12.5b	Direct Sensing of Particles, Fields and Waves Far Term Capability Roadmap		36
12.6a	In-Situ Instrumentation Near Term Capability Roadmap		41
12.6b	In-Situ Instrumentation Near Far Capability Roadmap		42
12.7	Science Instruments and Sensor Capability Breakdown Structure		45

# 12.1 General Portfolio Overview

## 12.1.1 Technology Capability Description

The Science Instruments and Sensors (SIS) roadmap (2005 NASA Capability Portfolio) includes capabilities associated with the collection, detection, calibration, conversion and processing of scientific data required to answer compelling science questions driven by the Vision for Space Exploration and The New Age of Exploration (NASA’s Direction for 2005 & Beyond).  Science Instruments and Sensors is a broad and diverse rubric with many enabling science measurement challenges. This technology investment portfolio, derived from the roadmap, is the result of a careful review and analysis of studies conducted by the National Academy of Sciences and by NASA (see 12.1.2.2) and of the extensive experience of the team members in scientific space instrumentation.

The Science Instrument and Sensors portfolio is organized into capabilities (12.X) and sub-capabilities (12.X.X) corresponding to the measurement wavelength range or specialized function.  The 6 top-level capabilities are:

  - Microwave Instruments and Sensors

  - Multi-Spectral Imaging / Spectroscopy (Vis-IR-FIR)

  - Multi-Spectral Sensing (UV-Gamma)

  - Laser / LIDAR Remote Sensing

  - Direct Sensing of Particles, Fields, and Waves

  - In Situ Instrumentation

The Capability Breakdown Structure (CBS; see 12.3.2 and Figure 12.7) was established to define the sub-capabilities and integrated technologies required to meet instrument or sensor performance criteria. For each capability, the roadmap shows driving design reference missions, science measurements, capability/technology gaps and a description of the developments (including alternate paths and options) required to advance the capability or technology to spaceflight.  Because of the requirement to develop strategic and capability roadmaps in parallel, it was not possible to prioritize a priori capability development on the basis of the highest ranked scientific strategies. Thus, the emphasis was placed on identifying science instrument and sensor capabilities that would enable multiple design reference missions, i.e., those having crosscutting applications.  This means that elements were prioritized by the degree to which they enabled or enhanced scientific discovery, by the breadth of their application across instrument and sensor capabilities and by the extent to which they met the needs of multiple Design Reference Missions (DRMs).

## 12.1.2 Benefits and Traceability

### 12.1.2.1 Enabled Missions/Science Goals

NASA’s pursuit of the Vision for Space Exploration cannot proceed without the development of new science instruments and sensors capabilities.  These capabilities are necessary for the collection and processing of scientific data, either to answer compelling science questions as old as human curiosity (e.g., How does life begin?) or to provide crucial knowledge to enable an exploration mission (e.g., remote surveys of Martian geology to identify optimal landing sites). Several of these capabilities are also required to support human missions through measurements of the safety of the environment and its suitability for human operations.

Critical science instrument and sensor capabilities were also found to have crosscutting applications in several other capability roadmaps.  For example, sensors developed for science applications can also be used for subsurface and atmospheric reconnaissance of planetary surfaces, a priority of the Robotic Access to Planetary Surfaces Roadmap (CRM #6).   Large format focal planes required by future instruments for IR to UV observations can provide critical feedback detection for active wave-front control systems required by the Advanced Telescope and Observatories Roadmap (CRM #4).

### 12.1.2.2 Traceability to Vision and Other Priority Agency Objectives

Science Instrument and Sensor capability needs can be traced directly back to the set of  top-level strategic documents listed in 12.5 below.  In addition to the Vision for Space Exploration, these sources include a variety of planning documents that express priority objectives of NASA and the research community.  Specific linkages between them and instrument needs are addressed via the Science Traceability Database, which is discussed in 12.1.3.

## 12.1.3 Assumptions, Qualifications, Provisions and Legacy Activities

The process by which the SIS Capability Roadmap was developed was discussed in the Executive Summary report (chapter 12 in NASA Capability Roadmaps Executive Summary – May 22, 2005); additional detail is given in Appendix 12.A.4.  Of primary importance here is the fact that the roadmap was formulated on the basis of strategic mission architectures derived from Strategic Roadmap Technical Interchange Meetings, Interim SRM Reports (dated April 15, 2005), and reviews of Final SRM Reports conducted during the period May 26 through June 3, 2005 with SRMs #2 (Robotic and Human Exploration of Mars), #3 (Solar System Exploration), #4 (Search for Earth-like Planets), #8 (Universe Exploration), #9 (Earth Science and Application from Space) and #10 (Sun-Solar System Connection).

A Comprehensive Design Reference Mission (DRM) Set of over 300 missions was compiled from NASA Advanced Planning and Integration Office (APIO) and Science Mission Directorate (SMD) documents (see 12.5.2), Advanced Mission Studies from the Mars Exploration Program Analysis Group (MEPAG), and reports from Strategic Roadmap Teams and at scientific professional meetings.  The missions that actually drive the development of enabling science instrument and sensor capabilities are given as the Design Reference Mission set shown in Table 12.A.1. The missions appear in alphabetical order with the earliest planned mission dates given by the appropriate strategic roadmap.  Also listed are the strategic and SIS Capability Roadmaps which  reference each mission.

A Science Traceability Database was developed to link compelling science questions, design reference missions, science instrument measurement needs, and critical instrument and sensor capability/technology gaps. This database draws on top-level strategic documentation, existing roadmaps, science measurement priorities described in design reference mission documentation, and science and engineering community input. An illustrative section of the database is shown in Appendix 12.A.2. The full database is available as a separate product.

A number of technologies were excluded from these roadmaps, primarily because they were covered by other roadmaps.  Thus, instruments and sensors performing “engineering” functions and instrument platform accommodations on a variety of platforms were handled by flight technology roadmaps; astronaut tools required to use instruments and sensors were handled by human systems roadmaps; and large sets of systems and associated technologies necessary to collect, concentrate and combine electromagnetic bands ranging from gamma-rays to radio waves (including gravity-waves) were handled by the telescopes and observatories roadmap.   The exception has been the inclusion of large antenna systems for microwaves in this roadmap, established in concert with the Advanced Telescopes and Observatories CRM.  Finally, the technical requirements of onboard data communications and storage, command and control software, transport of data from platform to Earth ground station, software for data analysis and data archiving have been presumed to be handled by roadmaps for communications and navigation and for advanced software systems.

## 12.1.4 Key Architecture/Strategic Decisions

Architectural and strategic decisions on the implementation of the Vision will guide the instrument and sensor development. Table 12.1.1 highlights those that are most important for this roadmap; the order does not indicate prioritization. Each strategic decision includes a description of the needed capability development. The decisions are driven by three primary factors: a) potential scientific discoveries, b) evolving programmatic emphasis, or c) the demonstration of technical feasibility. Dates are consistent with the strategic mission set shown in Table 12.A.1.

Table 12.1.1

Impacts of Key Architectural and Strategic Decisions

| Key Architecture / Strategic Decisions | Date Decision is Needed | Impact of Decision (Capability Development) |
| --- | --- | --- |
| Decision to accelerate capability for reliable 10–day weather forecasting. | 2005-2010 | Development of new synthetic aperture interferometric imagers for high spatial resolution imaging of global precipitation from GEO. Significant advances in the capability to measure wind speed and direction is required. Interconnection of numerical climate and forecast models with network of sensors into a sensor web is required. |
| Ability to forecast earthquakes, volcanic eruptions, tsunamis and related solid earth deformation events is shown to be feasible from remote sensing. | 2010-2015 | Develop capability to detect land surface deformation with high precision and frequency using either a small constellation of large MEO or GEO platforms or a dense LEO constellation of smaller platforms. Link spaceborne and ground based land deformation sensors using finite element solid earth model. |
| Decision to utilize accessible lunar volatiles for ISRU based on possible discovery by LRO or follow-on missions. | 2008 | Develop sample acquisition and handling systems that can operate for extended periods at ~40K. |
| Decision to establish a continuous human presence on the Moon. | 2015-2020 | Require next generation of detector systems for particles and fields to be used on missions to study the Sun-Earth environment to predict the safety of long-term human operations in space. |
| Decision to undertake a focused search for extant life on Mars, if prompted by the discovery of reduced organics, hydrothermal activity, or accessible extant aquifers. | 2005-2010 | Requires in situ instrumentation and sensors to detect life in a variety of places not currently accessible by available technology. |
| Decision to probe an accessible subsurface ocean on Europa, based on precursor remote mapping. | 2015-2020 | Develop novel subsurface sample acquisition systems and in situ instrumentation compatible with aqueous environments. |
| Build the capability to characterize an extrasolar earth-like planet, based on the discovery of such a body. | 2008-2015 | Develop sensor web of instruments, detectors, and optical systems (spatial interferometry, metrology, etc.) capable of detailed spectral and spatial observations of this planet. |
| Decision to prioritize investigations of cosmological gravity waves from the formation of the universe, black hole mergers, and from stars being devoured by black holes. | 2014 | High-sensitivity laser interferometry would be needed with developments in stable high-power lasers and spacecraft disturbance control, significantly beyond LISA capabilities. |
| Decision to prioritize probing the structure of early universe and map the distribution of dark matter. | 2010-2015 | Necessitates ultra-high-energy-resolution x-ray focal plane detectors; microcalorimeter arrays with associated continuous high-efficiency 50 mK coolers. |
| Decision to prioritize study of the nature of dark energy which is accelerating the expansion of the universe. | 2010-2015 | Need to measure both large-scale structures in the universe as well as the density of objects as a function of redshift. Development of large aperture optical systems with billion-pixel class focal planes. |

## 12.1.5 Major Technical Challenges

The highest priority technical challenges associated with Science Instrument and Sensors top-level capabilities are identified in Table 12.1.2, along with two crosscutting challenges shared by most of them. The challenges were selected by identifying those which, when met, will provide the capabilities needed to enable the highest priority design reference missions recommended by the science strategic roadmaps. A 15+ year roadmap of performance targets is also given for each of the challenges. Technical challenges are listed in order of the Level 1 CBS (see Figure 12.7) element to which they are most closely related (as indicated in parentheses). Their order in Table 12.1.2 does not indicate prioritization.

Table 12.1.2

Major Technical Challenges

| Major Technical Challenge | Requirements to Enable Driving Reference Missions |
| --- | --- |
|  | 2006-2010 | 2010-2020 | 2020 and Beyond |
| Large lightweight electronically scanned RF arrays (12.1) | 60% efficiency L-Band T/R modules; Lightweight apertures, membranes or panels (<8kg/m2) | 1 W Tx @ W-band T/R module; 250 mW DC digitizing receiver at 200 GHz | Very large apertures (~1000 m2) with integrated electronics, L-band and Ka-band. |
| Quantum limited heterodyne receivers (12.1) | 1x103 pixels @ 30 -100 GHz; low power dissipation | Broadband receivers near quantum limit to 12 THz ; > 4 octave spectrometry | Large low power, broad bandwidth, tunable arrays |
| Large format focal plane arrays (12.1, 12.2 & 12.3) | 5x108 BLIP CCD pxls at 140 K @ Vis/IR; 2eV X-ray resolution | 1x103 polarimetric BLIP array @ FIR; 1x108 pixel array @ IR; 1x109 pixel @ UV | 1x107 pixel X ray, 1eV resolution, response > 6 keV; Synthesize 1x107pixel mm-wave imager with thinned focal plane array; 1x108 pixel UV/Vis. |
| Improved LASER energy, lifetime, tuning, noise & efficiency (12.4) | 3 W @ 1-2 micron; lifetime > 5 yr move current technology to relevant environment demo | Tunable over 5 GHz; > 1 J/pulse | 300 W with 1:10-13 stability; lifetime > 5 yr |
| Miniaturized particles and fields instruments (12.5) | Thicker, larger SSD arrays with associated lower power, radiation-hard readout and processing electronics | Plasma isotopic composition | Energetic neutral atom conversion surfaces, imaging, composition |
| Comprehensive biomarker and organic assessment (12.6) | Bulk sample characterization of organic content at ppb levels | Broad survey sub ppt-level sensitivities in a flight package | Microfluidic, lab on a chip bioassay; biopolymer identification |
| Sample handling systems (12.6) | 40K sample handling with minimal volatile loss; 130K sample containment | Sample handling with minimal alteration or contamination; selective subsampling in core | Low-power drilling in environments <40 K with quantitative volatile preservation |
| Radiation-hard reprogrammable logic and massively parallel ASIC DSP (crosscutting) | 100 Mps/W microprocessor; 1-10 TIPS digital correlator, Hi-Rad ASIC | 8 GHz BW digital spectrometer; 100 TIPS digital correlator; 1 Mradiation-hard processor | 100 TIPS digital correlator @ < 50 W |
| Space qualified cryocoolers (crosscutting) | 5 K high efficiency cooler; continuous 50 mK cooler @ 5 microwatts load | 0.1 K cooler @ 100 mW load | Continuous 50 mK cooler @ 50 microwatts load |

## 12.1.6 Key Capabilities and Status

In this section we describe the ten most important sub-capabilities selected from a list of over 100 candidates. The following selection criteria were applied:

• Do they enable or enhance scientific discovery linked to the Vision for Space

Exploration?

• Do they have broad application across science instrument and sensors

capabilities?

• Do they meet the needs of multiple design reference missions?

These sub-capabilities are shown in Table 12.1.3, where Current Status refers to performance levels that have been demonstrated in a relevant space environment.  No prioritization among the 10 sub-capabilities was attempted.

Table 12.1.3

Status of Key Capabilities

| Capability | Sub-Capability | Missions Enabled | Current Status | Minimum Development Time (yr) |
| --- | --- | --- | --- | --- |
| 12.1 Microwave Instruments and Sensors | Integrated radar T/R modules | L-Band LEO InSAR, L-Band MEO InSAR, Ocean Structure and Circulation, LEO Cloud System Structure, InSAR Land Topomapper | 10-30W, 40% efficient; 4-5 chip MCM, $1K/module, Tx/Rx only | 3 |
| 12.1 Microwave Instruments and Sensors | Integrated radiometer receivers | Jupiter Polar Orbiter with Probes, Sea Ice Thickness, Einstein Inflation Probe, Global Tropospheric Aerosols, Mars Electrification Imager | THz Receivers: 100 element array at 100 GHz; 2 THz but not cryogenic; Digitizing MMIC Receivers: 500 mW at < 60 GHz | 5 |
| 12.2 Multi-Spectral Imaging / Spectroscopy (Vis-IR-FIR) | Visible, Near and Far-IR Detector Arrays and Readouts | TPF-C, Joint Dark Energy Mission, Magnetic Transition Region Probe, GEO Lightning Imager Large Aperture UV-Optical Observatory | Vis: 2k x 4k pixels, CCD; NIR: 2k x 2k pixels, photodiode/multiplexer FIR: ~ 400 pixels, bolometer array, NEP ~ 10-18 W/√Hz, unproven multiplexing | 5 |
| 12.1 Microwave Instruments and Sensors 12.2 Multi-Spectral Imaging / Spectroscopy (Vis-IR-FIR) 12.3 Multi-Spectral Sensing | Active Cooling Systems | Einstein Inflation Probe, Single Aperture Far Infrared Observatory, Neptune Orbiter with Probes, Joint Dark Energy Mission, Life Finder, Planet Imager, Constellation-X, Generation-X | >50K: standard flight technology 30-50K: in qualification 4K-30K: in lab development Intermittent sub-kelvin cooling: in service continuous sub-kelvin cooling: breadboard validation cryogen-free interface with mechanical cooler: proof of concept | 5 |
| 12.3 Multi-Spectral Sensing (UV-Gamma) | Large Format Focal Planes; High-Energy Resolution Pixelated Detectors | Large Aperture UV Optical Observatory, Stellar Imager, Magnetic Transition Region Probe | UV: 107 pixels MCP,15% QE; UV/X-ray: Megapixel CCDs, 10 W/Megapixel, 120 eV@6 keV resolution, 1 Hz readout speed, 150 nm - 6 keV; X-ray: 36 pixel micro-calorimeter, 6 eV @ 6 keV, 100 cps/pixel | 5 |

Table 12.1.3  (continued)

Status of Key Capabilities

| Capability | Sub-Capability | Missions Enabled | Current Status | Minimum Development Time (yr) |
| --- | --- | --- | --- | --- |
| 12.4 Laser / LIDAR Remote Sensing 12.5 Direct Sensing of Fields, Particles, and Waves | Lasers: Lifetime, High Power, High Frequency Stability | Lunar Recon Orbiter, Stratospheric Composition, Mars High Resolution Spatial Mapper, Laser Interferometer Space Antenna, Global Troposphere Winds, Stratospheric Composition, Photosynthetic Efficiency, Big Bang Observer, Europa Geophysical Explorer, Advanced Land Cover Change | 6x108 shots in space; 10-11 noise in lab; 30 mW in lab; no tunable or frequency stable designs space qualified. | 5 |
| 12.1 Microwave Instruments and Sensors 12.3 Multi-Spectral Sensing (UV-Gamma) 12.5 Direct Sensing of Fields, Particles, and Waves | Low power, radiation-hard electronics | L-Band MEO InSAR, Sea Ice Thickness, Global Tropospheric Aerosols, GEO Global Precipitation, Europa Geophysical Orbiter, Solar Probe, All multi-spacecraft missions | 1 Tera instructions per second; Microprocessor: ~ 10 Mps/W; DC/DC Conv.: effic. ~ 20 - 50%; A/D Conv.: 14 bits, 10 MHz, 250 mW; HVPS 150-400 gm Readout Analog Electronics: 106 channels, 100W/channel, 200 e rms noise/channel | 5 |
| 12.5 Direct Sensing of Fields, Particles, and Waves | Particle detectors with integrated electronics | Europa Geophysical Orbiter, Inner Heliosphere Sentinels (IHS), Solar Probe, Mag Con, Telemachus, Interstellar Probe (ISP), Heliospheric Imager and Galactic Observer (HIGO) | Solid state detector energy thresholds ≥ 10 keV; Limited arrays and higher power; Soft integrated electronics | 5 |
| 12.6 In Situ Instrumentation | Comprehensive biomarker and organic assessment | Mars Deep Drill, Mars Foundation Laboratory, Titan Explorer, Europa Pathfinder Lander, Europa Astrobiology Lander | Terrestrial lab-based systems for sub-ppt level sensitivity; non-comprehensive ppb-level sensitivity in bulk samples for flight prototypes | 5 |
| 12.6 In Situ Instrumentation | Sample handling with minimal sample alteration or contamination | Lunar Polar Explorer, Comet Surface Sample Return, Comet Cryo Sample Return, Mars Deep Drill, Europa Pathfinder Lander, Mercury Sample Return, Comet Surface Sample Return, Venus In-Situ Experiment Explorer, Europa Pathfinder Lander | MER rock abrasion tool, Phoenix sample acquisition | 5 |

# 12.2 Detailed Portfolio Discussions

## 12.2.1 Microwave Instruments and Sensors

### 12.2.1.1 Summary Description of Major Component Technologies

Microwave Instruments and Sensors include active microwave instruments (radar), passive radiometers, microwave navigation sensors (GPS) and crosscutting technologies such as cryogenic coolers and radiation-hard electronics. The frequency range

covered ranges from 30 kHz to 3 THz.  Key components include: antennas, receivers, transmitters and signal and data processing electronics.  Excluded from this portfolio are non-microwave electromagnetic science instruments, microwave instruments not designed for science (e.g., Entry, Descent and Landing Navigation Systems), and in situ microwave science instruments and sensors.

The Level 3 breakout of this portfolio is:

12.1.1 	Radar Altimetry

12.1.2 	Real Aperture Radar

12.1.3 	Synthetic Aperture Radar

12.1.4 	Interferometric SAR

12.1.5 	Radar Subsurface Sounding

12.1.6 	Passive Microwave Real Aperture Imager

12.1.7 	Passive Microwave Synthetic Aperture Imager

12.1.8 	Passive Microwave Sounder

12.1.9 	GPS – Radio-Time-of-Flight Triangulation

12.1.10 	Other Technologies

### 12.2.1.2 Benefits and Relationship to Missions and to Strategies

Key science questions (and representative missions) addressed by the Microwave Instruments and Sensors Portfolio include:

- Universe (Einstein Inflation Probe, SAFIR):

- What powered the big bang?

- How and when did galaxies first form?

- What are the properties of the earliest stars?

- Planetary Science (Jupiter Polar Orbiter/Probes, Neptune Orbiter/Probes, Europa Geophysical Orbiter):

- How long did it take Jupiter to form, and how was the formation of the Uranus and Neptune different from that of Jupiter and Saturn?

- Confirm the presence of interior oceans on Europa, measure ice thickness, elucidate formation of surface features

- Earth System Science (Sea Ice Thickness, Global Tropospheric Aerosols, Global Soil Moisture, Ocean Surface Winds, GEO Global Precip, mmWave GEO Radar, Land deformation InSAR, Ocean Structure and Circulation, Cloud System Structure):

- How does the cryosphere respond to and affect global environmental change?

- How do atmospheric trace constituents respond to and affect global environmental change?

- How are global precipitation, evaporation, and the cycling of water changing?

- How can weather forecast duration and reliability be improved?

- How are variations in local weather, precipitation and water resources related to global climate variation?

- How is the Earth's surface being transformed by naturally-occurring tectonic and climatic processes?

- How is the global ocean circulation varying on inter-annual, decadal, and longer time scales?

- What are the effects of clouds and surface hydrologic processes on Earth's climate?

### 12.2.1.3 Metrics and Major Requirements

Table 12.2.1 describes the primary metrics used to evaluate the various categories of microwave instrumentation, the present levels of satisfaction of those metrics and required levels of performance to address the science questions and mission requirements identified above.

Table 12.2.1

Metrics for Microwave Instrumentation

| Sub-Capability | Figures of Merit | Current Technology | Needed Technology |
| --- | --- | --- | --- |
| Interferometric SAR | Temporal and spatial resolution, swath width | Moderate High efficiency L-band T/R modules, Moderate ~30m2 antennas | Large (400–700m2), deployable antennas, High efficiency radiation-hard T/R modules, Digital Beam Formation (DBF) radiation-hard processor |
| Millimeter Wave RAR, SAR, and Interferometry | Electronic Beam Steering, Phase stability, Transmitted power, Receiver noise figure | Non-deployable antenna; mechanical beam steering, Discrete power amplifier (EIK) | Large deployable antenna, Electronic Beam Formation, High frequency T/R modules |
| Millimeter Wave Polarimeter Arrays, Spectrometers & Sounders | Noise limit, frequency resolution, bandwidth, number of pixels, degree of system integration; DC power requirement | Non-Quantum limit cryogenic receiver; moderate power consumption; 10s of pixels; individual assembly; moderate bandwidth digital autocorrelator | Quantum limit cryo receiver, 1000s pixels; highly integrated; wideband digital autocorrelator, radiation-hard processor, high efficiency cryocooler |
| Passive Synthetic Aperture Microwave Imagers | Spatial resolution, swath width, number of frequency/polarization channels, DC power, noise limit | TRL 6 synthetic aperture aircraft demos; TRL 4 MMIC correlating receivers, TRL 4 ASIC correlators | Low power MMIC receiver, massively parallel digital correlator, radiation-hard processor |

### 12.2.1.4 Current State-of-the-Art/Practice; Timeframe for Deployment

Table 12.2.2 presents detailed assessments of the current state of practice for specific enabling technologies linked to particular missions, and minimum estimated development times for achieving the level of performance to enable the relevant missions.

Table 12.2.2

Current State of Practice for Microwave Instrumentation

| Sub-Capability | Missions Enabled | State of Practice | Performance Required to Enable Mission | Minimum Estimated Development Time (yrs) |
| --- | --- | --- | --- | --- |
| Integrated radar T/R-modules | L-Band LEO InSAR, L-Band MEO InSAR, Ocean Structure and Circulation, LEO Cloud System Structure, InSAR Land Topomapper | 10-30W, 40% efficient; 4-5 chip MCM, $1K/module, Tx/Rx only | 10-30 W, 60% efficient; Single chip L-Band T/R, 2-5 W, 60% efficiency; T/R MMIC at K-Band, 2-5 W, 60% efficiency; W-Band T/R, 1 W, 20% efficiency; Ka-Band 5–10W, 40% efficiency., | 3 |
| Integrated radiometer receivers | Jupiter Polar Orbiter with Probes, Sea Ice Thickness, Einstein Inflation Probe, Global Tropospheric Aerosols, Mars Electrification Imager | THz Receivers: 100 element array at 100 GHz; 2 THz but not cryogenic; Digitizing MMIC Receivers: 500 mW at < 60 GHz | Quantum limited noise at 30-110 GHz; Low power MMIC Rx; 2 THz cryogenic receiver; 25-520 m at quantum limit; 10/100 GHz ultra low power MMIC Rx | 5 |
| Radiation-hard electronics | L-Band MEO InSAR, Sea Ice Thickness, Europa Geophysical Orbiter, Global Tropospheric Aerosols, GEO Global Precipitation | 1 Tera instructions per second; 100 MHz bandwidth for digital spectrometer | 1 MRad FPGA; 1 Tera-IPS correlator; Digital Spectrometer @ 2 GHz BW, 100 kHz res; Q~108 spectral resolution; 10 Tera-IPS correlator; 100 Tera-IPS correlator | 3 |
| Cryocoolers | Einstein Inflation Probe | Lab cryocooler | 4 – 10 K, high efficiency, space qualified | 3 |
| Precision deployable large structures | L-Band LEO InSAR, L-Band MEO InSAR, Ocean Salinity/Soil Moisture, InSAR Land Topomapper, GEO Global Precipitation | Rigid panels, 10-15 kg/m2 plus deployment structure | Active arrays (50 m2, 9 kg/m2, LEO; 400 m2, 4 kg/m2, MEO; 700 m2, 2 kg/m2, GEO; all 5 mm surfaces), Booms (10-100 m length, 1 kg/m; metrology compensation), Reflector antennas (700-7000 m2, 1-2 kg/m2, LEO, 5 mm surface; 500 m2, 10 kg/m2, > GEO, 1 µm surface, cooled < 10K) | 4 |

In the near-term and far-term capability roadmaps (Figures 12.1a and 12.1b), we present a graphical representation of the critical technical developments needed to achieve specific scientific measurement capabilities in support of particular driving missions.

Some technology elements were found to be critical (i.e., enabling) to specific DRMs, but not sufficiently cross-cutting to be assigned a high priority.  Of particular note among these are:

- For Global Soil Moisture Mission

- Precision deployable/inflatable structures (other than reflectors)

- Control of spinning apertures (balancing)

- For Solar Radio Bursts and Termination Shock Mission

- Large data storage

- For Next Generation Geodetic Networks/Observatory

- Next generation GPS/GNSS receivers

### 12.2.1.5 Demonstration and Precursor Mission(s)

The legacy and current missions underlying development of this technology capability to its current state are:

- Universe: WMAP, Herschel (aka FIRST), Planck, SOFIA (airborne)

- Planetary Science: Pioneer, Apollo–17, Magellan, Cassini, MARSIS

- Earth System Science: MSU, AMSU, MLS, MLS-2; SeaSat, DMSP, WindSat; SIR-A,B,C; SRTM; NScat, QuikScat; GeoSat, TOPEX, Jason; ESMR, TRMM, CloudSat

Some Earth Science and Planetary Science missions can serve as capability test beds for other missions.  We note the heritage from Nimbus NEMS and SCAMS to TIROS MSU to DMSP SSM/T, and from SeaSat SAR to Magellan SAR.  Similarly, the Jason MMICs provide a test bed for the JUNO Water/Ammonia Radiometer, and the MLS receivers and Spectrometers for similar instruments on the Jupiter and Neptune Orbiters.

## 12.2.2 Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR)

### 12.2.2.1 Summary Description of Major Component Technologies

Multi-Spectral Imaging/Spectroscopy (VIS-IR-FIR) includes sub-systems and components covering wavelengths from 0.4 to 1000+ μm. The key sub-capabilities are detector arrays, instrument-level optics and filters, mechanisms, (internal) calibration sources, electronics, as well as ancillary technologies, e.g., cryogenic coolers, and data processing systems.  Excluded from this category were Vis-IR near-field sensing systems or measurements within planetary atmospheres, both assumed to be covered by the

In-Situ Instrumentation roadmap.

The Level 3 breakout of this portfolio is:

12.2.1 	Visible Imagers, Photometers, Radiometers, Sounders

12.2.2 	Visible Spectrometers/Interferometers

12.2.3 	Visible Spectral and Hyperspectral Imagers

12.2.4 	IR/FIR Imagers, Photometers, Radiometers, Sounders

12.2.5 	IR/FIR Spectrometers/Interferometers

12.2.6 	IR/FIR Spectral and Hyperspectral Imagers

### 12.2.2.2 Benefits and Relationship to Missions and to Strategies

Key science questions (and representative missions) addressed by the Vis-IR-FIR Imaging/Spectrometry Portfolio include:

- Earth System Science (Black Carbon, Total Column Ozone, GEO Coastal Carbon, L2 Earth Atmosphere Solar Interferometer, LEO Cloud Particle Structure, GEO Lightning Imager):

- How do trace atmospheric constituents affect global climate change?

- How is climate change affected by trends in solar irradiation?

- How can weather forecasting be improved and made more reliable?

- Planetary Science (Jupiter Polar Orbiter/Probes, Europa Geophysical Explorer, Neptune Orbiter/Probes):

- What processes marked the initial stages of planet and satellite formation?

- Which processes produce and maintain habitable zones within the solar system?

- How long did it take for Jupiter to form and how did its formation differ from that of the other gas giant planets?

- Sun-Solar System Studies (MTRAP, Jupiter Polar Orbiter/Probes):

- What are the dynamics of the sun’s transition region?

- What are the similarities between auroral acceleration processes of different planets?

- Universe & Earth-like planets search (TPF-C, TPF-I, Einstein Inflation Probe, JDEM, Large Aperture UV Observatory, SAFIR, Life Finder, Planet Imager/Mapper):

- Is there evidence of life in other planetary systems?

- How are planetary systems formed, and what are their properties?

- Did the early universe undergo a process of rapid expansion?

### 12.2.2.3 Metrics and Major Requirements

Table 12.2.3 describes the primary metrics used to evaluate the various categories of

Vis-IR-FIR imaging and spectrometric instrumentation, the present levels of satisfaction of those metrics, and required levels of performance to address the science questions and mission requirements identified above.

Table 12.2.3

Metrics for Vis-IR-FIR Imaging and Spectroscopic Instrumentation

| Sub-Capability | Figures of Merit | Current Technology | Needed Technology |
| --- | --- | --- | --- |
| Visible Detector Arrays | Pixel Count, Uniformity, Quantum Efficiency, Noise, Crosstalk | ≤1 k x 2 k format ; Radiation degradation; Transition (CCD - CMOS); Few, changeable foundries | >2 k x 2 k format; Mosaics; Radiation tolerance; Stable fabrication infrastructure |
| IR Detector Arrays | Pixel Count, Noise, Power Dissipation, Temperature, Frame Time, Ability to sync to scene | ~104 pixels for some applications; ~106 pixels for astrophysics; Limited mosaics; Low-T’s required; Irregular effects | Large formats for all applications; Mosaics; Higher T arrays proven; Wider spectral response; Linear, fast response; High-throughput fabrication and testing |
| Far-IR Detector Arrays | Pixel Count, Uniformity, Quantum Efficiency, Noise, Crosstalk | Parallel investigations of best detection approaches; Early development of readout/mux approaches; Limited system demonstrations | Mature 104 pixel background-limited arrays; Demonstration of polarization, and 0.1-0.3 K cryogenics; High-T FIR broadband detectors; Stable fabrication and testing |
| ≥6 K Cryocoolers for Space | Cooling Power, Ultimate temperature, Thermodynamic Efficiency, Lifetime, Vibration | Limited flight experience; Significant reluctance to adopt in projects; Lifetime tests in lab preliminary but encouraging | Flight experience; No reluctance to adopt in projects; Long-life proven in lab (unattended) |
| Sub-kelvin coolers | Cooling Power, Ultimate temperature, Thermodynamic Efficiency, Lifetime | Few systems developed and qualified for flight; Alternate systems under investigation | Mature, high-efficiency systems for zero-g; Proven when staged to advanced 6 K coolers |
| Instrument Optics | Transmissivity, Spectral resolution, Element diameter and uniformity, Survives thermal cycling | Moderate size filters; Moderate capability dispersive instruments; Emerging active masks | Large, high- filters; Large, powerful dispersive instruments; Proven masks, and other techniques |

### 12.2.2.4 Current State-of-the-Art/Practice; Timeframe for Deployment

Table 12.2.4 presents detailed assessments of the current state of practice for specific enabling technologies linked to particular missions, and minimum estimated development times for achieving the level of performance to enable the relevant missions.

Table 12.2.4

Current State of Practice for Vis-IR-FIR Imaging and Spectroscopic Instrumentation

| Sub-Capability | Missions Enabled | State of Practice | Performance Required to Enable Mission | Minimum Estimated Development Time (yrs) |
| --- | --- | --- | --- | --- |
| Visible Detector Arrays and Readouts | TPF-C, Joint Dark Energy Mission, Magnetic Transition Region Probe, GEO Lightning Imager, Large UV-Optical Observatory | 2k x 4k pixel CCD, two-chip focal plane array, conventional drive electronics, ~ 5 electron noise | 5x108 BLIP CCD pixels at 140 K, ASIC, 4 electron noise (JDEM); High contrast FPA with coronagraph (TPF-C); 108 pixel visible array mosaic, photon counting (LUVO) | 5 |
| IR Detector Arrays and Readouts | Neptune Orbiter with Probes, Joint Dark Energy Mission, Life Finder, Planet Imager | 2k x 2k pixel near-IR array, lab crycooler, 320 x 240 micro-bolometer array 0.04 K NET(THEMIS) | 2x108 BLIP NIR pixels at 140 K, 4 electron noise, ASIC (JDEM); 106 room temp array, 0.02 K NET (Neptune Orbiter); 3-17 m BLIP arrays | 5 |
| FIR Detector Arrays and Readouts | Einstein Inflation Probe, Single Aperture Far Infrared Observatory | ~ 400 pixel arrays, NEP ~ 10-18 W/√Hz, unproven multiplexing, lab cryocoolers | 103 pixel BLIP array with polarization sensitivity (IP); 104 pixel BLIP array, 10-18 W/√Hz NEP, continuous cooling at T < 50mK (SAFIR) | 5 |
| Cryocoolers | Einstein Inflation Probe, Single Aperture Far Infrared Observatory, Neptune Orbiter with Probes, Joint Dark Energy Mission, Life Finder, Planet Imager | >50K: standard flight technology 30-50K: in qualification 4K-30K: in lab development Intermittent sub-kelvin cooling: in service continuous sub-kelvin cooling: breadboard validation cryogen-free interface with mechanical cooler: proof of concept | 4 – 10 K, high efficiency, space qualified Reliable and continuous 0.1K cooling | 3 |
| Instrument Optics and Filters, Advanced Visible and IR Spectrometers | TPF-I, Neptune Orbiter with Probes, L2 Interferometer, GEO Coastal Carbon, Magnetic Transition Region Probe, Single Aperture Far Infrared Observatory, Life Finder | Small scale instruments in space, < Megapixel arrays, ground-based interferometers | IR Imaging FTS, 106 pixels; 8 m boom, 0.1 m path stability; 103 pixel BLIP array, 10-20 W/√Hz; High throughput filter at 10 m, High contrast FPA Cryocooler at 4-6K | 7 |

In the near-term and far-term capability roadmaps (Figures 12.2a and 12.2b), we present a graphical representation of the critical technical developments needed to achieve specific scientific measurement capabilities in support of particular driving missions.

Sustained development of larger-format, higher-sensitivity focal plane arrays is key to meeting future instrument needs across the spectrum.  Important component (e.g., optics) and support (e.g., cryogenics) technologies are also critical; they need to be proven at the instrument-system level.  Other key technologies are on-board (or ‘intra-instrument’) calibration sources, imaging optics, data processing and compression systems (including, e.g., real-time feature extraction), and mechanical technologies enabling the deployment and control of the overall opto-mechanical structures.

### 12.2.2.5 Demonstration and Precursor Mission(s)

The legacy and current missions underlying development of this technology capability to its current state are:

- Earth System Science: LandSat, Ikonos, Quickbird 2, MODIS (Terra, Aqua), AIRS (Aqua)

- Planetary Studies: THEMIS, VIMS (Cassini), HiRISE and CRISM (Mars Recon Orbiter), TES (Mars Global Surveyor)

- Sun-Solar System Studies: LASCO, MDI/SOI (SOHO), SOT (Solar-B), SECCHI/STEREO

- Universe and Search for Earth-Like Planets: IRAC and IRS and MIPS (Spitzer), ACS (HST), NIRCam and NIRSpec and MIRI (JWST)

## 12.2.3 Multi-Spectral Sensing (UV-Gamma)

### 12.2.3.1 Summary Description of Major Component Technologies

Multi-Spectral Sensing (UV-Gamma) includes sub-systems and components for remote

imaging and spectrometry for the UV to Gamma ray wavelength range, λ < 0.4 μm (energies larger than 3 eV). The key technologies are detector arrays and associated electronics plus ancillary equipment such as cryogenic coolers.  It is assumed that lightweight, high-resolution grazing and normal incidence and diffractive optics (and coatings) are all covered by the Advanced Telescopes and Observatories roadmap, as are formation flying capabilities and the necessary metrology.  Technologies for cooling of large structures (including large-area detectors) and general thermal control are assumed to be handled by flight hardware roadmaps, and advanced data handling capabilities (high-speed telemetry, data compression, etc.) are handled by the communication and navigation roadmap.

The Level 3 breakout of this area is:

12.3.1 	UV Imaging and Spectrometry

12.3.2 	UV Interferometry

12.3.3 	X-Ray Imaging and Spectrometry

12.3.4 	X-Ray Timing and Polarimetry

12.3.5 	X-Ray Interferometry

12.3.6 	Gamma-Ray Imaging and Spectrometry

### 12.2.3.2 Benefits and Relationship to Missions and to Strategies

Key science questions (and representative missions) addressed by the UV-Gamma Ray Multi-Spectral Sensing Portfolio include:

- Universe & Earth-like planet search (Constellation-X, Black Hole Finder Probe, Large UV-Optical Observatory, Black Hole Imager, Advanced Compton Telescope, Generation-X, Stellar Imager):

- Determine origin of stars, planets, and life

- Determine origin of elements

- Probe early universe

- Map distribution of dark matter

- Perform black hole census

- Probe formation and evolution of black holes

- Probe space and time around black hole

- Sun-Solar System Studies (MTRAP, RAM, SCOPE):

- Measure and understand the magnetic transition region

- Determine the dynamics of the sun’s transition region

- Determine solar reconnection mechanisms

- Probe structure of region between heliosphere and local galactic environment

### 12.2.3.3 Metrics and Major Requirements

Table 12.2.5 describes the primary metrics used to evaluate the various categories of

UV-Gamma Ray imaging and spectrometric instrumentation, the present levels of satisfaction of those metrics, and required levels of performance to address the science questions and mission requirements identified above.

Table 12.2.5

Metrics for UV-Gamma Ray Imaging and Spectrometric Instrumentation

| Sub-Capability | Figures of Merit | Current Technology | Needed Technology |
| --- | --- | --- | --- |
| UV Imaging and Spectrometry | Large-format focal plane detectors; Microchannel plate performance | Limited by quantum efficiency and overall number of pixels | Factor of 10 increase in pixel number and factor of 2-5 increase in quantum efficiency |
| UV and X-ray Imaging and Spectrometry | Large-format focal plane detectors; CCD and active pixel sensor performance | Megapixel CCDs with moderate power requirements, moderate readout speeds, and limited UV and X-ray response | Larger CCDs with two orders of magnitude less power (possible change of technology to active pixel sensors), faster readout rate, and extended UV (< 200 nm) and x-ray (> 6 keV) response |
| X-Ray Imaging and Spectrometry | High-energy-resolution pixelated detector performance | Limited energy resolution, pixel array sizes and count rate capability | Factor of 2 and 4 (near and far term) improvement in energy resolution, 30 and 3x105 (near and far term) increase in pixel number and factor of ten increase in rate capability |
|  | Cryogenic cooler performance | Limited lifetime (laboratory prototype) continuous (50 mK) coolers; Cryocoolers requiring too much power and weight | Long-lifetime (7 year) systems; Reduced mass and power (factors of two) and increased robustness |
| Gamma Ray Imaging and Spectrometry | Readout electronics power, noise, yield and architecture | Systems cannot handle future channel counts and noise requirements; Low custom-chip yields (10-20%); Typical current architecture leads to long interconnects | Systems to handle 100 x more channels with low-noise interconnects; Factor of 2-5 increase in custom chip yield (due to large number needed); Novel ways to interconnect to reduce noise and provide near seamless arrays |

### 12.2.3.4 Current State-of-the-Art/Practice; Timeframe for Deployment

Table 12.2.6 presents detailed assessments of the current state of practice for specific enabling technologies linked to particular missions and minimum estimated development times for achieving the level of performance to enable the relevant missions.

Table 12.2.6

Current State of Practice for UV-Gamma Ray Imaging and Spectrometric Instrumentation

| Sub-Capability | Missions Enabled | State of Practice | Performance Required to Enable Mission | Minimum Estimated Development Time (yrs) |
| --- | --- | --- | --- | --- |
| Large Format UV Focal Planes, Microchannel Plates | Large Aperture UV Optical Observatory | 107 pixels, 10-15% quantum efficiency | 8x107 pixels, 50% quantum efficiency (LUVO) | 5 |
| Large Format UV Focal Planes, CCD/APS | Stellar Imager, Magnetic Transition Region Probe | Megapixel, > 150 nm response | > 108 pixels (UV), 6k x 6k, buttable, extended UV response (MTRAP) | 5 |
| Large Format X-ray Focal Planes, CCD/APS | Constellation-X, Black Hole Imager, Black Hole Finder, Generation-X | Megapixel, 120 eV @ 6 keV resolution, 1 Hz readout speed, 10 W/Megapixel, 6 keV response | 4k x 4k, 4-side buttable, <120 eV @ 6 keV (BHI); 30 Hz readout speed (Con-X); 0.1 W/Megapixel (BHI); X-ray response > 6 keV (Gen-X) | 5 |
| High Energy Resolution Pixelated Detectors | Constellation-X, Generation-X | 36 pixels, 6 eV @ 6 keV resolution, 100 cps per pixel (Astro-E2) | 2 eV, 103 pixels (Con-X); 1 eV, 107 pixels (Gen-X) > 1000 cps per pixel (Con-X) | 5 |
| Cryocoolers | Constellation-X, Generation-X | Cryogenic coolers: 50 mK, 5 W, near-continuous ADR, 300 W/W efficiency (cryocooler), lifetime not demonstrated | 50 mK, 5 W, continuous or duty cycle > 95%, 7 year lifetime, 500 W/W efficiency (Con-X) | 5 |
| Mega-to-Giga Channel Analog Electronics | Black Hole Finder Probe | 106 channels (GLAST), 100 W/channel. 200 electrons rms noise/channel (no connections) | 5x106 – 108, 100 W to 2 W/channel, < 300 e rms with interconnects and coupling (BHFP) | 5 |

In the near-term and far-term capability roadmaps (Figures 12.3a and 12.3b), we present a graphical representation of the critical technical developments needed to achieve specific scientific measurement capabilities in support of particular driving missions.

The key development for the UV through X-ray range is higher-performance focal plane detectors and their associated systems, with special emphasis on high energy-resolution detectors for high-energy photons.  For gamma-ray missions, the driving technology requirement is low-power electronics and architectures supporting mega-to-giga channel instruments.  Other key technologies are high-resolution, light-weight optics; formation flying and precision metrology for interferometry; on-board data process, storage, and high-bandwidth telemetry; cooling of large area detectors, and general thermal control; and on-ground (and in-flight) calibration of high-resolution detector systems and their associated optics.

### 12.2.3.5 Demonstration and Precursor Mission(s)

The legacy and current missions underlying development of this technology capability to its current state are:

- Sun-Solar System Studies: SOHO, IMAGE, RHESSI, Solar-B, STEREO

- Universe & Earth-like Planet Search: EUVE, HST, FUSE, Uhuru, Einstein, Chandra, Compton GRO, GLAST

## 12.2.4 Laser/LIDAR Remote Sensing

### 12.2.4.1 Summary Description of Major Component Technologies

Laser/LIDAR Remote Sensing encompasses sub-systems and components for surface elevation and atmospheric layer height measurements, transponder and interferometer operation for precise distance measurements, scattering for aerosol and cloud properties and composition, and Doppler velocity determination for wind measurement. Wavelengths range from 0.3 to 2 μm. The key technologies include lasers (high power, multi-beam and –wavelength, pulsed and continuous wave), detectors, receivers, and scanning mechanisms.  Excluded from this portfolio are laser systems for optical communication, range finders for landing systems, and laser/LIDAR in situ systems.  It is assumed that receiver optics and infrastructure are also addressed by the Advanced Telescopes and Observatories Roadmap, and that platform systems (especially to provide stability) are addressed by flight hardware roadmaps.  It is also noted that aircraft-based prototype systems are particularly important for validation of these technologies.

The Level 3 breakout of this technology area is:

12.4.1 	Altimeters

12.4.2 	Transponders

12.4.3 	Atmospheric LIDARS

12.4.4 	Spectrometers

12.4.5 	Interferometers

### 12.2.4.2 Benefits and Relationship to Missions and to Strategies

Key science questions (and representative missions) addressed by the Laser/LIDAR Remote Sensing Portfolio include:

- Earth System Science (CALIPSO/CALIOP, Tropical Winds, High Resolution CO2, Advanced Land Cover Change, Stratospheric Composition, Photosynthetic Efficiency):

- What do the distributions of ozone, aerosols and climate change imply about present-day climate?

- How do tropospheric winds affect weather?

- What do the distributions of trace gases imply for global warming?

- What is the three-dimensional structure of the world’s vegetation?

- What are the implications of photosynthetic efficiency for biological productivity?

- Planetary Science (Lunar Reconnaissance Orbiter, Europa Geophysical Orbiter, Mars High-resolution Spatial Mapper):

- What is the surface evolution of the solid planets and how does surface geology relate to planetary thermal evolution?

- What is the history of volatile compounds, especially water, across the solar system?

- What does the solar system tell us about the development and evolution of extrasolar planetary systems and vice versa?

- Universe & Earth-like planet search (LISA, Big Bang Observer):

- What happens at the edge of black holes?

- What is the nature of the pre-inflation universe?

### 12.2.4.3 Metrics and Major Requirements

Table 12.2.7 describes the primary metrics used to evaluate the various categories of laser/LIDAR remote sensing instrumentation, the present levels of satisfaction of those metrics, and required levels of performance to address the science questions and mission requirements identified above.

Table 12.2.7

Metrics for Laser/LIDAR Remote Sensing Instrumentation

| Sub-Capability | Figures of Merit | Current Technology | Needed Technology |
| --- | --- | --- | --- |
| Ranging Altimeters; Backscatter LIDARS | Time of flight; Signal intensity; Detector sensitivity | Single laser profiling systems | Multiple beams; Scanning or pixelated detectors with long lifetime |
| Doppler Wind Profilers | Doppler shift of narrow linewidth beam | Demonstrated from ground and aircraft; Orbital sensors under development | Longer lifetime; Increased resolution for Earth and planetary applications |
| Surface/ Atmosphere Reflectance Spectrometers | Detect presence of chemical component and concentration through absorption or fluorescence at targeted wavelengths | Demonstrated from aircraft | High-power systems with wavelength tunability and fine range gating |
| Interferometers | Precise measurement of distance | Demonstrated in lab | Advanced systems capable of operation in orbit and free space |

### 12.2.4.4 Current State-of-the-Art/Practice; Timeframe for Deployment

Table 12.2.8 presents detailed assessments of the current state of practice for specific enabling technologies linked to particular missions, and minimum estimated development times for achieving the level of performance to enable the relevant missions.

Table 12.2.8

Current State of Practice of Laser/LIDAR Remote Sensing Instrumentation

| Sub- Capability | Missions Enabled | State of Practice | Performance Required to Enable Mission | Minimum Estimated Development Time (yrs) |
| --- | --- | --- | --- | --- |
| Laser Lifetime | Lunar Recon Orbiter, Stratosphere Composition, Mars High Resolution Spatial Mapper, Big Bang Observer | 6 x108 shots in space, < 1 year | >109 shots in space, > 5 years | 5 |
| Laser Sampling Rate | Laser Interferometer Space Antenna, Advanced Land Cover Change, Mars High Resolution Mapper | 40 Hz (space qualified) | 75 – 100 kHz | 5 |
| High Power Laser | Laser Interferometer Space Antenna, Global Troposhere Winds, Stratospheric Composition, Photosynthetic Efficiency, Big Bang Observer | 30 mW | 3W – 300 W, 300 mJ/pulse, NIR 75 mJ/pulse, Vis 500 mJ/pulse | 5 |
| High Frequency Stability Laser | Europa Geophysical Explorer, Laser Interferometer Space Antenna Advanced Land Cover Change, Big Bang Observer | 1 part in 1013 (lab); laser noise: 10-11 m (lab); laser phase: 10-4 over +/- 50 kHz | Risk reduction demo; 1 part in 1013 (space); +/- 2 MHz over 1 GHz; 108 reduction laser noise; laser phase: 10-12 m over 1  | 5 |
| Laser Frequency Access | Global Tropospheric Winds, Stratospheric Composition, Photosynthetic Efficiency | Visible (space qualified) | NIR, Visible, UV | 7 |
| Detectors | Lunar Recon Orbiter, Europa Geophysical Explorer, Global Atmosphere Composition, LISA, Global Tropospheric Winds, Stratospheric Composition, Photosynthetic Efficiency, Mars High Resolution Spatial Mapper, Big Bang Observer | Visible, single element (space qualified); 32 x 32 array, photon counting (lab) | NIR, Visible, UV; Array > 100 pixels; Photon counting; Space qualified, > 5 years life | 3 |

In the near-term and far-term capability roadmaps (Figures 12.4a and 12.4b), we present a graphical representation of the critical technical developments needed to achieve specific scientific measurement capabilities in support of particular driving missions.

The key challenge is to develop reliable, efficient, space-qualified laser sources at the wavelengths required by the science measurements.  The identified tradeoffs dictate that competition must be used to choose optimal designs.  Funding transitions from low TRL (~1) to mid TRL (~4) is essential to risk and cost management.  Other key technologies include radiation-hard electronics, imaging optics, and the mechanical technologies required to deploy and control the overall opto-mechanical systems.

### 12.2.4.5 Demonstration and Precursor Mission(s)

The legacy and current missions underlying development of this technology capability to its current state are:

- Earth System Science: LITE, SLA, ICEsat/GLAS, CALIPSO/CALIOP, ALADIN/ADM-Aeolus

- Planetary Science: Clementine, NEAR, MGS MOLA, Messenger MLA, LRO LOLA

## 12.2.5 Direct Sensing of Particles, Fields and Waves

### 12.2.5.1 Summary Description of Major Component Technologies

Direct Sensing of Particles, Fields and Waves includes capabilities for in situ and remote sensing of particles (ions, electrons, neutral atoms, neutrons, cosmic rays); DC electric and magnetic fields, plasma waves, and gravity fields and waves. The sub-capability includes energetic particle and plasma imagers and spectrometers, high-energy particle detectors, magnetometers, electric fields and waves sensors, and gravitational waves and fields instruments.  It is presumed that the technology for measuring gravitational waves to meet the requirements of astrophysical experiments will be sufficient for measurements of the gravity field for planetary and earth science applications.  The associated laser technology is assumed to be handled either by the Laser/LIDAR Roadmap (for laser development) or the Advanced Telescopes and Observatories Roadmap (for transmit/receive telescopes and pointing systems).  It is also noted that a key aspect of direct particle and field measurement is the miniaturization and reduction in mass and power needs required to enable multi-spacecraft missions and missions that, because of the significant propulsion requirements levied by their extreme deployments, are very limited in their support to payload mass and power.  This miniaturization thrust is shared with the in-situ and remote sensing teams and with the development of spacecraft avionics.

The Level 3 breakout of this capability is:

12.5.1 	Energetic Particle and Plasma Imagers and Spectrometers

12.5.2 	High Energy Particle Detector Systems

12.5.3 	Magnetometers

12.5.4 	Electric Fields and Waves Instruments

12.5.5 	Gravitational Waves and Fields Instruments

### 12.2.5.2 Benefits and Relationship to Missions and to Strategies

Key science questions (and representative missions) addressed by the Direct Sensing of Particles, Fields and Waves Portfolio include:

- Universe (Laser Interferometer Space Antenna, Big Bang Observer):

- What is the geometry of the Universe and the nature of dark energy?

- Is there observational evidence supporting the hypothesis that the early universe underwent a period of rapid inflation?

- How do super massive black holes at the centers of galaxies form or evolve and what happens when they merge?

- Earth System Science

- What are the motions of the Earth's interior, and how do they directly impact our environment?

- Planetary Science (Jupiter Polar Orbiter/Probes, Europa Geophysical Explorer):

- How long did it take the gas giant, Jupiter, to form and how was the formation of the ice giants, Uranus and Neptune, different from that of Jupiter and its gas-giant sibling, Saturn?

- Sun-Solar System Studies (Solar Probe, Inner Heliosphere Sentinels, Telemachus, Interstellar Probe,  Heliospheric Imager and Galactic Observer, Ionosphere/Thermosphere Storm Probes, Radiation Belt Storm Probes, Geospace Electrodynamics Connection, Magnetospheric Constellation):

- What is the origin and societal impact of variability in the Sun-Earth system?

- How is the supersonic solar wind produced, and how does it evolve from the Sun’s transition region to the boundary of the heliosphere?

- How and where are solar energetic particles accelerated, what is their composition, how do they propagate through the heliosphere? What is their impact on the safety of extended manned exploration of the moon, Mars and beyond?

- What is the detailed structure of the heliosphere?  How does it change with time and modulate the intensity of galactic cosmic rays?

- What is the nature of the interstellar medium and how does the heliosphere interact with it?

- How do the space environment and ionosphere and upper atmosphere of the Earth respond to varying external and internal influences? What are the coupling mechanisms? How do interactions at other planets compare? What can magnetic field measurements tell us about the internal structure of these planets?

- What are the fundamental processes that operate in space plasmas?  How is energy transferred from stressed magnetic fields to heat plasmas and accelerate particles?

### 12.2.5.3 Metrics and Major Requirements

Table 12.2.9 describes the primary metrics used to evaluate the various categories of direct sensing instrumentation, the present levels of satisfaction of those metrics, and required levels of performance to address the science questions and mission requirements identified above.

Table 12.2.9

Metrics for Direct Sensing Instrumentation

| Sub-Capability | Figures of Merit | Current Technology | Needed Technology |
| --- | --- | --- | --- |
| Gravitational Waves and Fields | High sensitivity to low frequency (10-3 – 1 Hz) relative displacement of proof masses | Laser Interferometry | High power, stable, long-life lasers; Interferometer system; Disturbance compensation system (DISCOS); Telescope accuracy and pointing |
| Particle Detectors (plasmas, energetic electrons, ions, neutrals) | Energy/species/charge coverage and resolution; Solid angle coverage and resolution; Dynamic range | Electrostatic analyzers; Time-of-Flight (TOF) and Solid State Detector (SSD) telescopes | Compact sensors with better energy/angle coverage; Low threshold array detectors; UV blind gratings; Conversion surfaces; Highly integrated signal processing |
| Vector magnetometers Scalar magnetometers | Sensitivity; Absolute accuracy; Radiation tolerance; Orientation knowledge; Spacecraft magnetic field contamination | Vector: Fluxgate Scalar: He Precession 3 - 10 m boom | New fluxgate cores or alternate; Miniature scalar sensors; Mrad tolerant electronics; Multi-sensor systems: 0.5 to 1 m booms |
| Measurement of EM waves DC Electric Fields | Frequency coverage (DC-40 MHz); Sensitivity 3 axis Sensitivity | Mix of analog and digital electronics in pass bands, each with a different receiver; 50 m spin plane boom, 2.25 kg; 10 m spin axis boom, 5 kg | Highly flexible, digital coverage of entire bandwidth; Lower power, mass, cost; Lightweight electric field booms, reliable deployment for both spinning and non-spinning spacecraft |
| Lower power, radiation-hard electronics | Low power, Radiation-hard (>1 Mrad), High speed, High resolution, Reliable | Relatively high power processors; Low efficiency DC converters; High power A/D; HVPS limited reliability; Large | More standard components that are radiation-hard, low power, and miniature. |

### 12.2.5.4 Current State-of-the-Art/Practice; Timeframe for Deployment

Table 12.2.10 presents detailed assessments of the current state of practice for specific enabling technologies linked to particular missions and minimum estimated development times for achieving the level of performance to enable the relevant missions.

Table 12.2.10

Current State of Practice of Direct Sensing Instrumentation

| Sub-Capability | Missions Enabled | State of Practice | Performance Required to Enable Mission | Minimum Estimated Development Time (yrs) |
| --- | --- | --- | --- | --- |
| Gravitational Waves and Fields | Laser Interferometer Space Antenna (LISA) Big Bang Observer (BBO) | 30 mW laser, life < 1 yr; Interferometry: 10-11 m, 10Hz; Gravitational Reference Sensor: 10-10 m/s/s | 1 W laser, life ≥ 5 yr Interferometry 10-12 m, 10-3 Hz GRS: 10-15 m/s/s (LISA) 300 W laser, life ≥ 5 yr Interferometry 10-16 m, 1 Hz GRS: 10-17 m/s/s (BBO) | 5 |
| Particle Detectors (plasmas, energetic electrons, ions, neutrals) | Europa Geophysical Orbiter, Inner Heliosphere Sentinels (IHS), Solar Probe, Mag Con, Telemachus, Interstellar Probe (ISP), Heliospheric Imager and Galactic Observer (HIGO), Radiation Belt Storm Probes (RBSP) | Solid state detector energy thresholds ≥ 10 keV; Limited arrays and higher power; Soft integrated electronics | Ion implanted SSDs 15 µm to 5 mm thick; Large arrays; Low power, low noise, radiation-hard electronics; UV suppression grids; Stable charge conversion coatings | 3 |
| Vector Magnetometers Scalar Magnetometers | Europa Geophysical Orbiter, Geospace Electrodynamics Connection, Tropical ITM, Solar Probe, Mag Con, Interstellar Probe (ISP), RBSP | Fluxgate: 10 pT, 0.1 nT/week; Scalar (He): 1 pT, 1 ppm; 30 krad electronics; Boom: 3 - 10 m | Low noise core material; Multi-sensor system (Solar Probe, ISP); Radiation-hard electronics (~ Mrad) (EGO, RBSP); 1 pT vector sensitivity < 1 W (ISP); Low resource: < 0.2 W, < 0.1kg (Mag Con) | 3 |
| Measurement of EM waves DC Electric Fields | Solar Probe, Interstellar Probe (ISP) | A/D Converter: 8 bits, ≤ 20 Msps at 500 mW; DSP: Non-radiation hard, 1 W; Antenna: 50 m spin at 3 kg, 10 m axial at 5 kg | A/D: 18 bits @ 80 Msps @ < 100 mW DSP: Radiation hard, 250 mW, 103 pt. FFT at 3 MHz; Antenna: 50 m spin, ≤ 1 kg (inc. sensor); Axial ~ 20 m, rigid, ≤ 2 kg | 3 |
| Lower power, radiation-hard electronics | Europa Geophysical Orbiter, Solar Probe, All multi-spacecraft missions | Microprocessor: ~ 10 Mps/W; DC/DC Convert: efficiencies ~ 20 - 50%; A/D Converters: 14 bits, 10 MHz at 250 mW; HVPS; 150-400 gm | 100 Mps/W, on par with cell phone technology; Efficiencies ~ 85% A/D Converters: ≥ 14 bits, 80 MHz, 50 mW; HVPS Standard design, < 100 gm | 3 |

In the near-term and far-term capability roadmaps (Figures 12.5a and 12.5b), we present a graphical representation of the critical technical developments needed to achieve specific scientific measurement capabilities in support of particular driving missions.

Gravitational wave instruments will operate in a regime unattainable on Earth – key to their scientific success, but raising significant challenges for pre-flight test and validation.  The required technology, though, will be synergistic with other mission requirements.  The highly distributed nature of planned direct measurements of particles and fields throughout the solar system emphasizes the need to substantially reduce instrument mass, power, and cost.  It also raises the need to develop further the incorporation of many distributed sensors into a “sensor web”.  Other key technologies are MEMS, high quality mirrors (for laser interferometers) and miniaturization of spacecraft avionics.

### 12.2.5.5 Demonstration and Precursor Mission(s)

The legacy and current missions underlying development of this technology capability to its current state are:

- Earth System Science: GRACE, Polar, IMAGE, TIMED, Cluster

- Planetary Science: Galileo, Cassini, Messenger

- Sun-Solar System Studies: Voyager, Ulysses, ACE

## 12.2.6 In Situ Instrumentation

### 12.2.6.1 Summary Description of Major Component Technologies

In Situ Instrumentation required by future NASA missions ranges from close range electromagnetic sensors to the full gamut of analytical chemistry and modern molecular biology techniques.  They incorporate technologies essential to NASA science missions involving landed planetary exploration, sample return, and atmospheric probes, as well as technologies that support prospecting for in-situ resources.  Techniques for acquiring, handling, processing, and storing samples are required. In addition to miniaturizing traditional laboratory size equipment, the instruments must be capable of operating in extreme environmental conditions of temperature, radiation, pressure, and corrosiveness, potentially with stringent planetary protection requirements.  Excluded from consideration were sensors for astronaut health and safety and general curatorial facilities for sample return (including quarantine facilities and mission-specific environmental maintenance).

The Level 3 breakout of this instrumentation area is:

12.6.1 	Imaging/Microscopy

12.6.2 	Mineralogical/Elemental Analysis

12.6.3 	Chemical Detection and Identification

12.6.4 	Isotope Analysis/Age Dating

12.6.5 	Biological Detection and Identification

12.6.6 	Geophysical Measurements

12.6.7 	Sample Handling and Preparation

12.6.8 	In-Situ Instrument Engineering

### 12.2.6.2 Benefits and Relationship to Missions and to Strategies

Key science questions (and representative missions) addressed by the In-Situ Instrumentation Portfolio include:

- Planetary Science (Astrobiology Field Lab, Groundbreaking Mars Sample Return, Deep Drill, Long-Lived Lander Network, Lunar South Pole-Aitken Basin Sample Return, Comet Surface Sample Return, Comet Cryogenic Sample Return, Asteroid Sample Return, Venus Surface Sample Return, Mercury Sample Return, Lunar Seismic Network, Venus In-Situ Explorer, Jupiter Polar Orbiter/Probes, Neptune Orbiter/Probes, Europa Pathfinder Lander, Titan Explorer, Europa Astrobiology Lander, Uranus Orbiter/Probes, Neptune Orbiter w/ Triton Lander):

- What processes marked the initial stages of planet and satellite formation?

- Where are the habitable zones for life in the solar system and what are the planetary processes responsible for producing and sustaining habitable worlds?

- How long did it take the gas giant, Jupiter, to form and how was the formation of the ice giants, Uranus and Neptune, different from that of Jupiter and its gas-giant sibling, Saturn?

- How did the impactor flux decay during the solar system’s youth and in what way(s) did this decline influence the timing of life’s emergence on Earth?

- What is the history of volatile compounds, especially water, across the solar system?

- What is the nature of the organic material in the solar system? Its history?

- What global mechanisms affect the evolution of volatiles on planetary bodies?

- Does (or did) life exist beyond Earth?

- Why did the terrestrial planets differ so dramatically in their evolution?

- How do the processes that shape the contemporary character of planetary bodies operate and interact?

- What does the solar system tell us about the development and evolution of extrasolar planetary systems and vice versa?

### 12.2.6.3 Metrics and major requirements

Table 12.2.11 describes the primary metrics used to evaluate the various categories of

in situ instrumentation, the present levels of satisfaction of those metrics, and required levels of performance to address the science questions and mission requirements identified above.

Table 12.2.11

Metrics for In Situ Instrumentation

| Sub-Capability | Figures of Merit | Current Technology | Needed Technology |
| --- | --- | --- | --- |
| Biomarker Detection and Characterization | Sensitivity; Selectivity; Contamination ID and quantification | Characterization of viable organisms that can be cultured; Terrestrial contamination exceeds detection limits | Quantitative assessment of all organic material; Technology to ensure isolation from terrestrial contamination |
| Sample Handling and Preparation | Operability in relevant environment; Degree of sample alteration; Subsampling accuracy | Bias from particle size and density; Qualitative ability to preserve volatile fractions; Operability over limited temperature ranges | No bias or fractionation in end-to-end sample handling chain, even in multi-phase samples; Ability to selectively subsample in primary sample acquisition; Operability from 40K to 750K |
| Planetary Protection | Sensitivity to detection of viable organisms; Breadth of detection of viable organisms; Degree of sterilization | Characterization of viable organisms that can be cultured; Detection levels well below sterilization levels | Characterization of any viable organisms; Sterilization levels on par with detection levels |
| Chemical Identification at Small Spatial Scales | Spatial resolution; Sensitivity; Selectivity or mass resolution | Micron-level chemical and isotopic assessment in terrestrial labs; AFM for crude surface analysis | Micron-level chemical and isotopic assessment in flight package |
| Miniaturization, Ruggedization, and Payload Integration | Mass; Power; Volume; Shock/Vibration tolerance; Survivability in extreme environments | Payload elements developed separately, little common mass and power elements | Payload elements developed together minimize mass and power resources |

### 12.2.6.4 Current State-of-the-Art/Practice; Timeframe for Deployment

Table 12.2.12 presents detailed assessments of the current state of practice for specific enabling technologies linked to particular missions and minimum estimated development times for achieving the level of performance to enable the relevant missions.

Table 12.2.12

Current State of Practice for In Situ Instrumentation

| Sub-Capability | Missions Enabled | State of Practice | Performance Required to Enable Mission | Minimum Estimated Development Time (yrs) |
| --- | --- | --- | --- | --- |
| Biomarker Assessment | Mars Deep Drill, Mars Foundation Laboratory, Titan Explorer, Europa Pathfinder Lander, Europa Astrobiology Lander | Lab-based commercial systems | ppb sensitivity and miniaturization to flight scales (MFL) | 5 |
| Sample Handling | Lunar Polar Explorer, Comet Surface Sample Return, Comet Cryo Sample Return | Cryomechanisms: MER mobility system | 40K demo (LPE) | 3 |
|  | Mars Deep Drill, Mars Foundation Laboratory, Europa Pathfinder Lander, Mercury Sample Return | Subsampling: MER RAT | mm-scale sampling of sedimentary layers (MFL) | 5 |
|  | Comet Surface Sample Return, Venus In-Situ Explorer, Europa Pathfinder Lander, Mars Foundation Laboratory | Sample Phase Preservation: Phoenix sample acquisition | No heating of samples above –20C (MFL) | 5 |
| Planetary Protection | Jupiter Orbiter w/Probes, Mars Foundation Laboratory | Sensitive assays: subset of viable spores cultivated | Full range of viable life characterized (MFL) | 3 |
|  | Jupiter Orbiter w/Probes, Mars Foundation Laboratory, Mars Sample Return | Contamination control in sample handling: organic contamination in lunar sample of 10s of ppb | Sub-ppb organic contamination in returned samples (MSR) | 3 |
| Chemical ID at small spatial scales | Mars Foundation Laboratory | Miniaturized imaging systems Phoenix AFM; Miniaturized composition probes: Lab-based system | Submicron imaging combined with chemical/isotopic analysis (MFL) | 5 |
| Miniaturization and Payload Integration | Mars Sample Return, Mars Deep Drill, Titan Explorer | Galileo and MER payloads | 10x smaller than Galileo, Downhole Instrument Suite, balloon payload | 5 |

In the near-term and far-term capability roadmaps (Figures 12.6a and 12.6b), we present a graphical representation of the critical technical developments needed to achieve specific scientific measurement capabilities in support of particular driving missions.

In situ instrument development will be a key enabling technology for exploration missions to the Moon, Mars, and beyond; specific driving missions may change, but the driving science likely will not.  Robust mid-TRL programs are needed to close the gap between needed and available capabilities for lunar and non-Mars destinations (e.g., a MIDP-like program for New Frontiers).  In situ performance should be validated in environmentally-relevant test beds prior to competitive selection (e.g., instrument breadboard sensitivity and precision should be proven in a realistic Mars test bed).

The most challenging developments for in situ instrumentation will be contamination control and the mechanical and electronics developments that enable operation in the wide variety of extreme environments (radiation, temperature, pressure, liquid medium) relevant to the various missions.  Other key technologies will relate to payload system integration and distributed processing.

### 12.2.6.5 Demonstration and Precursor Mission(s)

The legacy and current missions underlying development of this technology capability to its current state are:

- Planetary Science: Viking, Mars Pathfinder, MER, Phoenix, MSL, Apollo Sample Return, Genesis, Stardust, Pioneer Venus Probes, Galileo Probe, Huygens Lander

# 12.3 Roadmap Process

## 12.3.1 Summary History of Roadmap Team, Meetings and Presentations

The SIS Capability Roadmap was initiated with a kickoff meeting on September 28, 2004, at which team member recommendations were collected from NASA, academia, and industry.  Basic planning activities carried out at that time were the development of the Level 1 Capability Breakdown Structure and the determination of the overall schedule and required budget.  Public input to the process was solicited for a workshop held on  November 30, 2004, which had 112 registrants, 23 capability presentations and 67 white papers submitted.  This process was considered particularly important as the development of scientific instruments and sensors is a peer-reviewed process that emerges more from the proposal process than from strategic planning activities.  The CRM Team held its first roadmapping workshop at JPL on December 8-9, 2004, at which time the team reviewed the planning documents, CBS, and roadmap development process and listened to a number of science and technology presentations.  The sub-teams met on their own, primarily via teleconferences, to define the Level 2 CBS, develop the spreadsheets for the Science Traceability Database and review the strategic reference documentation.  A second CRM workshop was then held at GSFC on January 4-6, 2005. The team  presented status of the Capability Roadmap and Strategic Roadmap Teams, reviewed and discussed the Science Traceability Spreadsheets developed by Aerospace Corp., completed several CBS related tasks, and established a 3-month detailed schedule leading to the NRC Review in March 2004. In addition to presentations on the NASA Science Vision and on various capabilities and technologies, the team worked on the Science Traceability Database and examined the connection points with other CRMs.  At a third CRM workshop on February 2-4, 2005, the team completed the CBS to Level 4, reviewed the Science Traceability Database, identified high-priority capabilities and began preparation for a review of its work by the NRC.

On March 16, 2005, the SIS draft capability roadmap was presented to a panel of external reviewers put together by the NRC.  The key questions that the NRC panel was asked to address were: Has the roadmap identified a clear pathway to development of the needed capabilities?  Have the maturity levels of the technologies been correctly assessed?  Have appropriate metrics been defined for measuring the advancement of technical maturity levels?  Have the connection points with other capability and strategic roadmaps been properly identified?  An extensive debriefing of the NRC panel after the presentations was used to guide and correct the SIS roadmap.

On March 31, 2005, the SIS Chair presented the status of the roadmapping effort to the SMD senior external advisory committee in Washington, DC. The Space Science Advisory Committee/Earth System Science and Applications Advisory Committee (SScAC/ESSAAC) reports to the NASA Advisory Council (NAC).  The presentation was well-received and the committee was very impressed with the roadmapping effort.

Through extensive teleconferences, the SIS CRM team drafted an Executive Summary Roadmap, which was submitted to the NASA Advanced Planning and Integration Office on May 14, 2005 and, after some modification, to the NASA Administrator on June 1, 2005.  Additional teleconferences were held with representatives of the SRM teams for Exploration of Mars, Exploration of the Solar System, Search for Earth-Like Planets, Exploration of the Universe, Earth Science and Applications, and Sun-Solar System Connection in order to verify that the priorities established by the SIS roadmap were not in conflict with the mission architectures established by the SRMs.  These guided the final preparation of this report.

## 12.3.2 Capability Breakdown Structure (CBS)

The Science Instruments and Sensor Capability Breakdown Structure, shown in Figure 12.7, represents an attempt to group similar technologies which, for electromagnetic sensors, also maps closely to wavelength ranges. This approach produced a total of six capabilities; each one generally covers a very wide range of wavelengths and technologies, all supporting and linked to diverse science and exploration strategic objectives.

Figure 12.7

Science Instruments and Sensor Capability Breakdown Structure

## 12.3.3 Connection to Other Roadmaps

In order to explicate the overlaps and interfaces with other elements of the NASA roadmapping activity, Table 12.3.1 highlights capability and strategic roadmaps with which important interrelationships with the Scientific Instruments and Sensors Roadmap have been identified.  Those contributions deemed critical have been highlighted in red in the left-adjoining column; those contributions considered moderate have been highlighted in green.  CRMs and SRMs for which the interrelationships were considered marginal have not been listed at all.

Table 12.3.1

Interrelationships to Other Capability (CRM) and Strategic (SRM) Roadmaps

| CRM |  | Contributions to SIS |  | Contributions from SIS |
| --- | --- | --- | --- | --- |
| In-Space Transportation |  |  |  |  |
| Advanced Telescopes and Observatories |  | Telescopes and platforms, with particular reliance on large deployable precision structures, and wavefront sensing and control systems. Also critical are formation flying interferometers and active cryo systems |  | Instruments for which telescopes are deployed; microwave antenna systems; control systems using focal-plane data; telescope metrology systems |
| Communication and Navigation |  | High bandwidth communications for high data-rate sensors. |  |  |
| Robotic Access to Planetary Surfaces |  | Access to in-situ samples, both surface and subsurface |  | Instruments for subsurface and atmospheric reconnaissance |
| Human Planetary Landing Systems |  |  |  | Instruments for surface and atmospheric recon; robotic precursors systems |
| Human Health and Support Systems |  |  |  |  |
| Human Exploration Systems and Mobility |  |  |  |  |
| Autonomous Systems and Robotics |  | Radiation-hard processors |  |  |
| In Situ Resource Utilization |  | Collection of material for in situ analysis |  | Synoptic surveys for resource mapping; in situ analysis for resource assessment |
| Advanced Modeling, Simulation, and Analysis |  |  |  |  |
| Systems Engineering and Cost/Risk Analysis |  |  |  |  |
| Nanotechnology |  | Devices, sensors, actuators, electronics |  |  |
| SRM |  | Impact of SRM on SIS Work |  | Reliance of SRM on SIS Products |
| Lunar Exploration |  | In situ analysis; imaging spectrometers; astronomical platforms |  |  |
| Mars Exploration |  | In situ analysis; imaging spectrometers; high spectral resolution sensors |  | Laser altimeters; in situ sampling systems; geological surveying; atmospheric characterization and monitoring |
| Solar System Exploration |  | In situ analysis; imaging spectrometers; high spectral resolution sensors |  | Laser altimeters; in situ sampling systems; surface surveying; atmospheric characterization and monitoring |
| Search for Earth-Like Planets |  | Wide-FOV optics; long-baseline imaging optical interferometers; high spectral resolution sensors |  | Wide field-of-view surveys; very high spatial resolution imaging; high sensitivity, high spectral resolution spectrometry |
| Universe Exploration |  | Wide-FOV imagers; interferometric gravity wave detection; background-limited sensors across the spectrum |  | Large-scale detector arrays; high stability, high precision lasers for gravitational wave detection; sub-mK sensors and coolers |
| Earth Science and Applications |  | InSAR; high-resolution passive spatial interferometer; mm-Wave spectrometer; High spectral resolution sensors; high-speed, high-sensitivity LIDARs and DIALs; stable, long-term calibration |  | High precision land deformation; trace gas atmospheric composition; penetration to surface through extreme weather events; tropospheric wind profiler |
| Sun-Solar System Connection |  | Sub-VHF radio systems; solar radar; high-speed imagers/spectrometers. |  | Imagers; spectrometers; RF systems; magnetometers; particle analysis |
| Education |  |  |  |  |
| Nuclear Systems |  |  |  |  |

12.4 Summary and Recommendations

## 12.4.1 Major Conclusions and Recommendations

The Science Instruments and Sensors Capability Roadmap Team used current NASA exploration and science measurement strategies, design reference missions, and science instrument/sensor technology roadmaps to identify critical science measurement capability gaps and assess future technology development needs.  It was clear that prioritization of technical developments required careful traceability to science measurement needs; therefore, in support of this, the team developed a Science Traceability Database as a separate product.

Several key sub-capabilities were identified that are traceable to the Vision for Exploration and cut across instrument capabilities and science applications.  These are summarized in Table 12.4.1.

Table 12.4.1

Key Sub-Capabilities

| Capability | Sub-Capability Technical Requirements | Capability | Sub-Capability Technical Requirements |
| --- | --- | --- | --- |
| Microwave Instruments and Sensors | Large deployable antennas | Lasers/LIDAR Remote Sensing | High energy lasers (for atmospheric sensing, formation flying, etc.) |
|  | Integrated high efficiency T/R modules |  | Quality control of laser systems (all components) |
|  | Radiation-hard electronics |  | Frequency stability and selection |
|  | Quantum limited cryogenic receivers |  | Spatial coverage: multibeam, scanning, pixelated detectors |
|  | High frequency, low power MMIC receivers |  | High-sensitivity detectors |
|  | Large scale digital spectrometers and correlators (radiation-hard FPGAs and ASICs) | Direct Sensing of Fields, Particles and Waves | High power lasers |
|  | Low power, long life cryocoolers |  | Spacecraft disturbance compensation systems |
| Multi-Spectral Imaging/ Spectroscopy (Vis-IR-FIR) | Low power, long life cryocoolers |  | Detectors and detector arrays, light weight rigid booms |
|  | Detectors & Readout Electronics (large format, better sensitivity) |  | Compact, radiation-hard, high integration electronics and sensors |
|  | Optics (dispersive/ imaging; instrument level including filters, coolers, polarimeters) | In Situ Instrumentation | Sample handling in wide range of extreme environments |
| Multi-Spectral Sensing (UV – Gamma Ray) | Large format CCDs / active pixel sensors |  | Sample acquisition on the surface of Mars |
|  | High-energy-resolution single-photon detectors |  | Miniaturization for instruments and integrated payloads (nano)electronics; better integrated across the board |
|  | Low-power, long-life cryogenic coolers to achieve less than 0.1K |  |  |
|  | Mega-to-giga channel analog electronics |  |  |
|  | Optics (Normal/grazing incidence, higher-energy optics, gratings |  |  |

Certain major technical challenges were highlighted.  For example, several planetary missions require that science payloads (and especially in situ instruments) operate in environments far more severe than previously attempted.  These include the high radiation environment of near-Jupiter orbit, the high temperature (730 K) and pressure (90 bars) surface of Venus, the extremely cold (< 100 K) surfaces and atmospheres of the outer planets and their satellites, and the immersion in liquid required for subsurface exploration (e.g., of Europa).  Also, the extremely resource-constrained circumstances of planetary missions (especially for the outer solar system) require payloads of limited mass and volume that can operate at limited power levels and data rates.  This has a particular impact on the use of cryogenically cooled sensors.

While the focus has been on specific technical issues, it is important to note the challenges associated with the general process of instrument development and deployment.  High fidelity instrument system models are required to perform early risk assessments and technical resource trade analyses.  A robust flight demonstration program is essential to risk reduction and involves both airborne and orbital flights.  The latter will continue to be a pacing item for the introduction of new technologies required to reduce capability gaps.  Finally, significant infrastructure investments are required to develop performance testing capabilities.  When coupled with some of the collection systems called out by the Advanced Telescopes and Observatories Roadmap, it is clear that ground-based test facilities will be hard pressed to verify performance for many of the instruments incorporated into high-priority missions.  Table 12.4.2 lists the critical facility needs for which significant physical infrastructure planning is required.

Table 12.4.2

Critical Facility Needs

| Capability | Critical Facility Need | Existing Facilities | Physical Infrastructure Planning |
| --- | --- | --- | --- |
| 12.1 Microwave Instruments and Sensors 12.2 Multi-Spectral Imaging / Spectroscopy (Vis-IR-FIR) 12.3 Multi-Spectral Sensing (UV-Gamma) | Stable and high-throughput fabrication infrastructure for large format detector arrays, detector arrays, readout multiplexers, and miniaturized instrument optics High-throughput testing for large format detector arrays | NASA: GSFC (DDL), JPL (MDL) for detector arrays and miniaturized instrument optics; NIST: Detector arrays and superconducting readout multiplexers University: MIT Lincoln Labs, Caltech and UC Berkeley for detector arrays Industry: Rockwell, Raytheon, and BAE for large format IR detector arrays and multiplexer readouts NASA: GSFC (DCL), JPL, ARC University: Princeton, Caltech, UC Berkeley, MIT, Univ. Hawaii Industry: Vis-IR-UV | Critical for continued development of large format detector arrays. DOD community and commercial industry has little interest in FIR detectors. Sole source in NIST for superconducting readout multiplexers. Detector fabrication and testing infrastructure requires substantial financial investment, which typical research awards cannot support Many scientific detector arrays (microwave, FIR, IR, X-ray) operate at cryogenic temps, which requires cryogenic testing infrastructure |
| 12.1 Microwave Instruments and Sensors | Large RF, environmentally-controlled facility for development and testing of large deployable antennas |  |  |
| 12.2 Multi-Spectral Imaging / Spectroscopy (Vis-IR-FIR) 12.4 Laser / LIDAR Remote Sensing | Instrumented calibration regions Aircraft and ground-based prototype testing | Rogers Dry Lake CA, Stennis Space Center MS, Cuprite NV, Barreal Blanco Argentina, Mt. Fitton and Lake Frome Australia, ocean sites near Hawaii and Bermuda | Critical for instrument calibration of the full field of the instrument over the full spectral range, especially for spectrometric imagers |
| 12.5 Direct Sensing of Fields, Particles and Waves | High charge state ion beam facility, keV energies; Neutral beam facility, 1 eV to 1 MeV; Solar corona simulator | U. Bern RF powered source, GSFC has hollow cathode source U. Denver O/H facility inoperative owing to PI death | Establish NASA high-charge state facility for community use Establish NASA neutral atom source and beam facility for community use |
| 12.6 In Situ Instrumentation | Environmentally relevant instrument test beds to simulate conditions on Moon, Mars, Venus, etc. | Mars Yard at JPL; various non-dedicated thermal vacuum chambers | Environmentally relevant test bed will provide an important service to the community and reduce mission risk |

One important challenge that bridges the domains of this analysis and those of data communications and advanced software is the significant future opportunity posed by the linkage of orbital and ground-based observations into “sensor webs”.  This is seen in a wide range of instrumentation frameworks, including Earth system studies, planetary studies, and Sun-solar system studies.

This team concluded that a sustained advanced technology program will be required to narrow or close the identified science instrument and sensors capability gaps and enable several strategic missions.  Many of the specific capabilities required must be brought from low TRL levels to TRL~6, at a rapid pace, to meet the integration timescales of their driving missions.  This is particularly true for technology to support human exploration of Mars, for which many of the significant decisions must be made decades before the missions themselves.

Extensive involvement by the science communities during the process of assessing capability gaps reinforced critical aspects of NASA’s science instrument and sensors strategic investment processes. The competed, peer-reviewed development programs that rely on NASA, government, commercial and academia partnerships are essential to develop the technology capabilities necessary to achieve NASA’s priority science program.  This approach also seems to be key for securing reliable funding over the long term.

Finally, in addition to laying out an evolutionary scheme for technology development to meet the demands of the future NASA mission architectures, some consideration was given to identifying those areas where revolutionary developments would have great impact.  Table 12.4.3 lists these “breakthrough” technology areas; more detailed descriptions are documented elsewhere.

Table 12.4.3

"Breakthrough" Technologies for Future Mission Architectures

| Capability | “Breakthrough” Technology |
| --- | --- |
| 12.1 Microwave Instruments and Sensors | Fourier synthesis microwave imaging |
|  | Large aperture multi-frequency radar |
| 12.2 Multi-Spectral Imaging/Spectroscopy (vis-IR-FIR) | Holographic optics |
|  | Uncooled imaging detectors |
|  | Mega-pixel, photon-counting radiation-hard CCDs |
|  | Quantum computing for detectors |
|  | Three-dimensional imaging |
| 12.3 Multi-Spectral Sensing (UV-Gamma) | Three-dimensional imaging |
| 12.4 Laser/LIDAR Remote Sensing | High-power, high-reliability laser diodes |
|  | High-efficiency, non-linear optical components |
|  | High storage time fiber architectures |
|  | Synthetic aperture LIDAR |
| 12.5 Direct Sensing of Particles, Fields and Waves | Swarms of miniaturized, autonomous sensors |
|  | Extremely low energy neutral atom (ELENA) and pickup ion imaging |
|  | Comprehensive organic and biomarker ID in a compact package |
| 12.6 In Situ Instrumentation | Detailed subsurface sounding of structure & composition |
|  | In-situ chemical ID at micron scales, e.g., downhole |
|  | MEMS high-specificity comprehensive gas-phase and liquid-phase ID |
|  | Precise age dating in compact package |
|  | Targeted single atom/molecule ID in terrestrial sample return analysis with minimal sample preparation |
|  | Selective sample concentration techniques, such as solvent extraction |
|  | Targeted in-situ sub-sampling |
|  | Sample handling at hot/cold extremes |
|  | Handling of multiphase samples |
|  | Sample handling/containment zero forward/backward contamination |
|  | Milliwatt power sources |

## 12.4.2 Next Steps

Rough order-of-magnitude costing of the development plan laid out in this document will be reported separately.  This must be reconciled with investment guidance from NASA management.  While there has been some attempt to identify obvious disagreements with the recommendations of the Strategic Roadmaps, there is a clear need for a more extensive interchange and resolution of conflicting assumptions.  There are, as well, some overlaps and interfaces with other Capability Roadmap analyses that need to be examined to ensure consistency and coverage.  Analyses of gaps in this development plan with respect to the strategic roadmaps, of the proper linkage and prioritization of developments with respect to those plans, and of the reasonableness of the timescales for development to meet the needs of the missions identified by those strategic plans are proper subjects for review by the NRC.

# 12.5 Acknowledgement/References

## 12.5.1 Acknowledgement

The information contained herein is the product of 9 months of hard work from the SIS CRM Team composed of NASA, industry, other government agencies and academic experts nationwide. We want to thank the SIS CRM Team for their dedication and contributions to the development of the Science Instruments and Sensor Capability Portfolio 2005.  Our compliments go to the leadership and membership of the SIS Team on both the depth and breadth of their efforts to support the goals of the Agency, NASA’s Science Program and its Capability Roadmapping efforts. We look forward to potential future collaborations between NASA, industry, other government agencies and academia to implement the recommendations from this long-range, strategic planning process.

We want to thank the SMD Coordinators, Mr. Harley Thronson, Mr. Giulio Varsi, and Mr. Jens Feeley, for their leadership and guidance. We want to thank Mr. Perry Bankston, from NASA JPL, for his coordination efforts on behalf of the NASA Advanced Planning and Integration Office (APIO).  Special thanks go to: Ms. Heather Lancaster, from NASA Peer Review Services, for setting up the funding mechanisms for the External Team Members; Ms. Amanda Peterson and Ms. Monica Washington, from the NASA Peer Review Services, for helping with all the conference/workshops logistics; Ms. Shelly Standiford and Ms. Donna Drummond, from NASA GSFC, for their overall administration and resources support; and last, but not least, Ms. Mary Pat Hrybik-Keith, Ms. Ruth Jennings, and Ms. Deborah Clark, from NASA GSFC, for their graphics and editorial support.

## 12.5.2 References

### 12.5.2.1 Strategic Documents

The Vision for Space Exploration (February 2004), NASA NP-2004-01-334-HQ

A Journey to Inspire, Innovate, and Discover: Report of the President’s Commission on Implementation of United States Space Exploration Policy (June 2004), U. S. Government Printing Office, ISBN 016-073075-9.

Strategic Plan for the U.S. Climate Change Science Program, Climate Change Science Program and the Subcommittee on Global Change Research (7/24/03)

Our Changing Planet: The US Climate Change Science Program for Fiscal Years 2004 and 2005

### 12.5.2.2 National Research Council Reports

Astronomy and Astrophysics in the New Millennium, Astronomy and Astrophysics Survey Committee, Board on Physics and Astronomy, Space Studies Board (2001), National Academy of Sciences

Connecting Quarks with the Cosmos: Eleven Science Questions for the New Century, Committee on the Physics of the Universe (2003), National Academy of Sciences

Implementing Climate and Global Change Research: A Review of the Final U.S. Climate Change Science Program Strategic Plan, Committee to Review the U.S. Climate Change Science Program Strategic Plan (2004), National Academy of Science

New Frontiers in the Solar System: An Integrated Exploration Strategy, Solar System Exploration Survey, Space Studies Board (2003), National Academy of Science

Solar and Space Physics and Its Role in Space Exploration, Committee on Assessment of the Role of Solar and Space Physics in NASA's Space Exploration Initiative (2004), National Academy of Science

The Sun to the Earth -- and Beyond: A Decadal Research Strategy in Solar and Space Physics, Solar and Space Physics Survey Committee (2002), National Academy of Sciences

The Sun to the Earth -- and Beyond: Panel Reports, Solar and Space Physics Survey Committee, Committee on Solar and Space Physics (2003), National Academy of Sciences

### APIO Design Reference Missions

Architecture Study #2, Human Exploration of Mars, Artificial-Gravity Nuclear Electric Propulsion Option (7/15/03)

Earth-Sun System: Potential Roadmap and Mission Development Activities (12/23/04)

Reference Mission Version 3.0  Addendum to the Human Exploration of  Mars (6/01/98)

Lunar Surface Reference Missions:  A Description of Human and Robotic Surface Activities (07/01/03)

Mars 98 Reference Mission: Reference Mission of the NASA Mars Exploration Study Team (7/7/97)

The Mars Surface Reference Mission:  A Description of Human and Robotic Surface  Activities (12/01)

Solar System Exploration - 2000 to 2035 (Draft 3)

Universe Design Reference Missions (12/13/04)

### Advanced Mission Studies: Mars Exploration Program Analysis Group

Astrobiology Field Laboratory-2013 (Biosignature Detection)

Ground Breaking Mars Sample Return

Mars Deep Drill: Explore Active Hydrothermal Habitats

Mars Deep Drill: Search for Evidence of Past Life

### Enterprise Strategies

Beyond Einstein:  From the Big Bang to Black Holes (2003), Structure and Evolution of the Universe Roadmap Team

Earth Science Application Plan

Earth Science Enterprise Strategy (2003)

Earth Science Research Plan (Draft, 1/6/05)

Earth-Sun System: Potential Roadmap and Mission Development Activities, Earth Science Technology Office (Draft, 12/23/04)

Sun-Earth Connection Roadmap (2003-2028)

Physics of the Universe: A Strategic Plan for Federal Research

Solar System Exploration Roadmap

Origins Roadmap (2003)

Structure and Evolution of the Universe Roadmap

# 12.A	Appendices

## 12.A.1 Design Reference Mission Set

Table 12.A.1 lists the missions referred to in the capability roadmaps shown in section 12.2.  In addition to the name, the table gives the current planned launch date, the Strategic Roadmap whose architecture includes the mission, the sub-capability responding to the mission and an indication of whether the mission appears in the SIS Executive Summary report. Missions listed with an * are not traceable to the CRM Planning Milestones, however, they represent major options for architectural decisions in subsequent years.

Table 12.A.1

Design Reference Mission Set

| Mission | Launch Date for Planning | Strategic Roadmap | Capability Roadmap |
| --- | --- | --- | --- |
| Advanced Compton Telescope (ACT)* | 2026 | 8 | 12.3 |
| Advanced Land Cover Change | 2017 | 9 | 12.4 |
| Big Bang Observer (BBO) | 2025 | 8 | 12.4 12.5 |
| Black Hole Finder Probe (BHFP) | 2018 | 8 | 12.3 |
| Black Hole Imager (BHI) | 2025 | 8 | 12.3 |
| Comet Cryogenic Sample Return (CSSR) | 2020 | 3 | 12.6 |
| Comet Surface Sample Return (CSSR) | 2013 | 3 | 12.6 |
| Constellation-X | 2017 | 8 | 12.3 |
| Einstein Inflation Probe (EIP) | 2016 | 8 | 12.1 12.2 |
| Europa Astrobiology Lander | 2030 | 3 | 12.6 |
| Europa Geophysics Explorer | 2012 | 3 | 12.1 12.2 12.4 12.5 |
| Europa Pathfinder Lander | 2022 | 3 | 12.6 |
| Geospace Electrodynamics Connections (GEC) | 2016 | 10 | 12.5 |
| Generation-X* | 2027 | 8 | 12.3 |
| GEO Coastal Carbon | 2018 | 9 | 12.2 |
| GEO Global Precipitation | 2027 | 9 | 12.1 |
| GEO Lightning Imager | 2027 | - | 12.2 |
| GEO Seismology from Space* | 2030 | 9 | 12.1 |
| GEO Surface Deformation* | 2025 | 9 | 12.1 |
| Global Atmospheric Composition | 2013 | 9 | 12.4 |
| Global Tropospheric Aerosols* | 2016 | 9 | 12.1 |
| Global Tropospheric Winds | 2015 | 9 | 12.4 |
| Heliospheric Imager and Galactic Observer (HIGO) | 2032 | 10 | 12.5 |
| Inner Heliospheric Sentinels (IHS) | 2015 | 10 | 12.5 |
| Interstellar Probe (ISP) | 2028 | 10 | 12.5 |
| Joint Dark Energy Mission (JDEM) | 2020 | 8 | 12.2 |
| Jupiter Icy Moons Orbiter* | 2017 | 3 | 12.1 |
| Jupiter Polar Orbiter with Probes | 2014 | 10 | 12.1 12.6 |
| Large Aperture UV-Optical Observatory (LUVO) | 2020 | 4, 8 | 12.3 |
| Mission | Launch Date for Planning | Strategic Roadmap | Capability Roadmap |
| Laser Interferometer Space Antenna (LISA) | 2014 | 8 | 12.4 12.5 |
| L-Band LEO InSAR* | 2012 | 9 | 12.1 |
| L-Band MEO InSAR* | 2014 | 9 | 12.1 |
| LEO Cloud System Structure* | 2023 | 9 | 12.1 |
| LEO Wetland and River Monitor* | 2015 | 9 | 12.1 |
| Life Finder | 2025 | 4 | 12.2 |
| Lunar Polar Explorer* | 2012 | - | 12.6 |
| Lunar Reconnaissance Orbiter (LRO) | 2009 | 1 | 12.4 |
| Magnetospheric Constellation (MagCon) | 2021 | 10 | 12.5 |
| Magnetic Transition Region Probe (MTRAP)* | 2020 | 10 | 12.2 12.3 |
| Mars Deep Drill | 2018 | 2 | 12.6 |
| Mars Electrification Imager | 2022 | - | 12.1 |
| Mars Foundation Laboratory | 2020 | 2 | 12.6 |
| Mars High Spatial Resolution Mapper* | 2023 | - | 12.4 |
| Mars Sample Return (MSR)* | 2016 | 2 | 12.6 |
| Mercury Sample Return* | 2025 | - | 12.6 |
| Neptune Orbiter and Probes | 2018 | 3 | 12.1 12.2 |
| Ocean Salinity/Soil Moisture* | 2017 | 9 | 12.1 |
| Ocean Structure and Circulation* | 2019 | 9 | 12.1 |
| Ocean Surface Winds | 2018 | 9 | 12.1 |
| Photosynthetic Efficiency* | 2020 | 9 | 12.4 |
| Planet Imager | 2035 | 4 | 12.2 |
| Reconnection and Microscale (RAM)* | 2025 | 10 | 12.2 12.3 |
| Sea Ice Thickness* | 2014 | 9 | 12.1 |
| Single Aperture Far InfraRed Observatory (SAFIR) | 2023 | 4 | 12.1 12.2 |
| Solar Connections Observatory for Planetary Environments (SCOPE) | 2033 | 10 | 12.3 |
| Solar Polar Imager (SPI) | 2026 | 10 | 12.5 |
| Solar Probe | 2018 | 10 | 12.5 |
| Stellar Imager (SI) | 2030 | 8, 10 | 12.3 |
| Stratospheric Composition* | 2018 | - | 12.4 |
| Telemachus* | 2026 | 10 | 12.5 |
| Terrestrial Planet Finder – Coronagraph (TPF-C) | 2016 | 4 | 12.2 |
| Terrestrial Planet Finder – Imager (TPF-I) | 2019 | 4 | 12.2 |
| Titan Explorer* | 2020 | 3 | 12.6 |
| Triton Lander* | 2032 | 3 | 12.6 |
| Tropical ITM Couplet* | 2017 | 10 | 12.5 12.6 |
| Venus Aeronomy Probe (VAP) | 2032 | 10 | 12.6 |
| Venus In Situ Experiment | 2018 | 3 | 12.6 |

## 12.A.2 Science Traceability Matrix

The Science Traceability Database was developed to establish, track, and communicate linkages between compelling science questions, design reference missions, science instrument measurement needs and critical instrument and sensor capability/technology gaps.  The database draws on top-level strategic documentation, existing enterprise roadmaps, science measurement priorities described in design reference mission documentation and science and engineering community input.  It relates compelling science questions and associated design reference missions to science instrument measurement needs and critical instrument and sensor capabilities/technologies gaps.  Additional details on the preparation of this product are included in 12.A.4 as part of the discussion of background assumptions.

An illustrative section of the database is shown in Table 12.A.2.  Not shown in the table, but present in the full database, are linkages for each Science Question to the Strategic Roadmaps, NASA Science Reference Documents and Scenario Documents.  Each measurement scenario is assessed as to the presence of a technology gap and a number is assessed as to specific orbital requirements for the measurement platform.  The full database is available as a separate product.

Table 12.A.2

Sample Excerpt from Science Traceability Database

| Science Question | Relevant Missions | Launch Date | Measurement Parameter | Measurement Scenario | Target Body | Technology Component Development |
| --- | --- | --- | --- | --- | --- | --- |
| How are global precipitation, evaporation, and the cycling of water changing? How are variations in local weather, precipitation and water resources related to global climate variation? | GEO Global Precipitation Doppler Radar/ Passive Imager | 2027 | Rainfall and wind in hurricanes; Temp profile; moisture profile; precipitation under clouds | Large Ka-band spiral-scan radar; Microwave sounder, 50 and 183 GHz | Earth's atmosphere | Spiral scan via mechanical scanning of transmit and receive feeds; 30 m lightweight deployable membrane antenna; 50 and 183 GHz MMIC radiometers with < 4 dB NF; 1-bit digital cross-correlators with 200 MHz BW |
| What are the dynamics of Sun's magnetic transition region between photosphere and upper chromosphere? | Magnetic Transition Region Probe | 2020 | Velocity (vector if possible) and vector magnetic fields in chromosphere/ corona | Doppler Imager/ Magnetograph | Sun | Large, lightweight UV reflective optics; Up to 16K x 16K CCDs with high QE at 150 nm and low power |
| What is the structure of the early Universe? What are the properties of space time near a black hole? | Con-X | 2017 | Imaging Spectroscopy | Measure the x-ray spectra of distant quasars and earliest galactic clusters X-ray spectra of matter near black hole | Quasars, galactic clusters Black holes | CCD focal plane detectors with 30 Hz readout rate. Microcalorimeter with 103 pixels, 2 eV resolution, and 103 c/s rate capability. Cryogenic coolers with long-life (7 years), continuous (or duty cycle > 95%) operation, and high efficiency (500 microwatt/watt) |

Table 12.A.2  (continued)

Sample Excerpt from Science Traceability Database

| Science Question | Relevant Missions | Launch Date | Measurement Parameter | Measurement Scenario | Target Body | Technology Component Development |
| --- | --- | --- | --- | --- | --- | --- |
| How can terrestrial weather forecast duration and reliability be improved? | Global Tropospheric Winds | 2013 | Atmospheric wind profile | Direct Doppler or coherent LIDAR | Earth | 2 µm laser 2 J/pulse with 12 Hz PRF and 3 year life; 0.75 m lightweight diffraction-limited optics; tunable cw laser for local oscillator; high precision optical alignment; conical scanning; lag-angle compensation; etc. |
| How do fields and particles in inner heliosphere change with time? What is the distinction between flare and shock accelerated particles? | Inner Heliosphere Sentinels | 2015 | Fields and Particles | In Situ Instruments | Helio-sphere | Ion implanted solid state detectors, 15 µm to 5 mm thick; Large arrays; Low power, low noise, radiation-hard electronics; UV suppression grids |
| How do the processes that shape the contemporary character of planetary bodies operate and interact? | Mars Sample Return | 2016 | Chemistry, mineralogy, and chronology of the crust, the role of volatiles, and potential biomarkers | Samples from carefully chosen sites will be returned to Earth | Mars | Sample handling with minimal sample contamination or alteration; micron-scale mineralogical, elemental and isotopic assessment for sample selection |

## 12.A.3 Sub-Capability Team Expertise

Microwave Instruments and Sensors

Name			Organization			Primary Expertise

Soren Madsen		NASA JPL	(co-lead)	Radar

Chris Ruf		Univ. Michigan (co-lead)	Atmosphere and Ocean Radiometry

Dave Glackin		Aerospace			Earth Remote Sensing Satellites

Suzanne Staggs	Princeton			Cosmic Microwave Background

Azita Valinia		NASA GSFC			Earth Science Technology

Juan Rivera		NASA GSFC			Instruments Design/Engineering

Shyam Bajpai		NOAA SIS			Operational Weather Satellites

Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR)

Name			Organization			Primary Expertise

Craig McCreight	NASA ARC (co-lead)		IR Detectors for Astronomy

Ron Polidan		Northrop Grumman (co-lead)	UV-Visual-IR Sensors,

Instrumentation Systems

Bruce Spiering	NASA Stennis			Vis-IR Remote Sensing

Instrumentation, Oceans

Steve Ackerman	U. Wisconsin			Meteorology, Cloud Science,

Aerosols

Rich Dissly		Ball Aerospace		In situ, and Atmospheric

Applications

Tim Krabach		NASA JPL			LWIR to FIR Detectors

Multi-Spectral Sensing (UV-Gamma Ray)

Name			Organization			Primary Expertise

Brian Ramsey		NASA MSFC	(co-lead)	XRay-Gamma Ray Instrumentation

David Chenette	Lockheed Martin (co-lead)	Space Radiation Measurements

Ron Polidan		Northrop Grumman		UV Instrument Systems

Juan Rivera		NASA GSFC			Instruments Design/Engineering

Azita Valinia		NASA GSFC			Earth Science Technology

Laser/LIDAR Remote Sensing

Name			Organization			Primary Expertise

Maria Zuber 		MIT (co-lead)			Laser Ranging and Altimetry

Richard Barney	NASA GSFC (co-lead)	Laser Instrument Design

Richard Dissly		Ball Aerospace		In situ and Atmospheric

Instrumentation

Direct Sensing of Particles, Fields and Waves

Name			Organization			Primary Expertise

Richard McEntire	JHU/APL (co-lead)		Particle Instrumentation

Carl Stahle		NASA GSFC (co-lead)	Detector Systems

Tim Krabach		NASA JPL			LWIR to FIR Detectors

Paul Mahaffy		NASA GSFC			Analytical Systems

Dave Chenette		Lockheed Martin		Space Radiation Measurement

In-Situ Instrumentation

Name			Organization			Primary Expertise

Tim Krabach		NASA JPL (co-lead)		Astrobiological Systems

Rich Dissly		Ball Aerospace (co-lead)	Analytical Systems

Paul Mahaffy		NASA GSFC			Analytical Systems

Richard McEntire	JHU/APL			Particles and Fields

Dave Chenette 	Lockheed Martin		High-Energy Detectors

## 12.A.4 Detailed Assumptions of the Roadmapping Process

### 12.A.4.1 Scope

- The material prepared by the CRM 12 Team will be based upon the team members’ technical expertise and instrument development experience and has to be traceable to the Vision for Space Exploration.

- There are two criteria to meet in evaluating candidate Instrument/sensor technologies.  Highest priority is given to technologies that will:

  - Achieve goals closely aligned with the Exploration Vision.

  - Constitute a major advance and/or enable a large number of missions/goals.

- Specific science instrument and sensor groups include the following:

  - Microwave Instruments and Sensors

  - Multi-Spectral Imaging/Spectroscopy (Vis, IR, FIR)

  - Multi-Spectral Sensing (UV-Gamma)

  - Laser/LIDAR Remote Sensing

  - Direct Sensing of Fields, Waves and Particles

  - In Situ Instrumentation

- The Science Instruments and Sensors Roadmap scope will not include:

  - Instruments and sensors performing “engineering” functions

  - Instrument accommodations on a variety of platforms (orbiting, landers, rovers, probes, aerial vehicles)

  - Astronaut tools required to use instruments and sensors

  - Large sets of systems and associated technologies necessary to collect, concentrate and combine electromagnetic bands ranging from gamma-rays to radio waves and including gravity-waves

### 12.A.4.2 SIS Library

- Regarding information exchange and status, JPL’s secure DocuShare website will be used as the repository for:

  - Individual Roadmap Data Storage

  - Information Exchange

  - Overall Schedule Update

  - Issue Resolution Postings

  - APIO Briefings

### 12.A.4.3 Science Traceability Spreadsheets

- All Science Instrument and Sensors capability needs can be traced directly back to the following top-level strategic documentation (detailed list is shown in backup charts):

  - The Vision for Space Exploration

  - A Journey to Inspire, Innovate, and Discover: President’s Commission Report

  - The New Age of Exploration: NASA Strategic Objectives for 2005 and Beyond

  - Our Changing Planet: The US Climate Change Science Program for Fiscal Years 2004 and 2005

  - Design Reference Missions

  - Moon and Mars Science Working Groups

  - NASA Enterprise Strategies

  - National Research Council Reports

- Science Traceability Spreadsheets were developed to establish, track and communicate linkages between compelling science questions, design reference missions, science instrument measurement needs and critical instrument and sensor capabilities/technologies gaps.

  - NASA Design Reference Missions, existing enterprise roadmaps, science measurement priorities and science and engineering community input was collected, reviewed and documented.

  - Interim Earth, Planetary Science, Sun-Solar System and Astrophysics spreadsheets were presented to several Strategic Roadmap Teams for review.

- The spreadsheets deal with missions that launch by 2030, but not beyond. Aerospace Corp developed four spreadsheets covering: Earth Science, Planetary Science, Sun-Solar System Connection and Astrophysics.

- Earth Science:

  - Science questions are organized into the six ESE science focus areas.

  - All missions are Design Reference Missions (DRMs).  Only those missions that have Power Point charts associated with them in the DRM document (NASA ESTO December 23, 2004 briefing) are included; the others fly too soon to be influenced.

- Sun-Solar System Connection:

- Some non-DRM missions are listed but can be ignored because they have launch dates after 2030 or have uncertain launch dates.

- Comparative magnetospheres missions have been included.

- Orbital information is given for this spreadsheet only, because it can be varied and interesting.

- Planets:

- All missions are DRMs.

- There were no firm launch dates; the earliest proposed year is given.

- No technology development items are proposed in the documents, except for vague generalities, thus none are listed for the planetary area.

- Astrophysics:

- All missions are DRMs, except those shown in red.  (Note that ground-based instruments and near-term space missions like JWST, are not DRMs.)

### 12.A.4.4 References from the Master Spreadsheets

### 12.A.4.5 Roadmap Development Overall Process

- Capability Roadmap Team Kickoff (September 28, 2004)

  - Establish the SIS Team

    - Select and invite the External Co-Chair

    - Collect team member recommendations from NASA, academia and industry

    - Select NASA and external team members

  - Preliminary Planning activities

    - Develop the Capability Breakdown Structure, Roadmap Development Plan, Budget, and Schedule

    - Investigate Roadmap Overlap

- Public Workshop (November 30, 2004)

  - 112 people registered to the SIS session

  - 67 White Papers submitted

  - 23 Capability Presentations

  - Follow-up activity with presenters

- First Team Workshop (JPL)  (December 8-9, 2004)

  - Team Introductions

  - Review Planning Documents

  - CBS

  - Science and Technology Presentations

  - Roadmap Development Process

  - Sub Teams Selection

  - Sub Team Activities

    - Define the Capability Work Breakdown Structure (CBS) Level 2 and Dictionary

    - Develop the Science Traceability Spreadsheets

    - Review Strategic Reference Documentation

  - NRC Presentation Planning and Preparation

    - Review the template and develop the data products

    - Prepare initial Sub-team presentations for review

- GSFC Workshop (January 4-6, 2005)

  - Status from NASA HQ, APIO, Capability Roadmap Teams and Strategic Roadmap Teams.

  - Review and discuss Science Traceability Spreadsheets developed by Aerospace Corp.

  - Complete the following Capability Breakdown Structure related tasks:

    - Level 1 Statement of Scope

    - Level 2 Definition (including dictionary)

    - Establish linkages between the Capability Breakdown Structure Level 2 and science/exploration needs via the Science Traceability Spreadsheets and Design Reference Missions.

    - Begin to capture Level 3 content.

  - Discuss roadmap development plan and near term milestones such as the NRC review in March, 2004.  Establish 3-month, detailed schedule with deliverables.

  - Presentations on Science Vision, Science Capability and Technology content.

- MIT Workshop (February 2-4, 2005)

  - Development of the CBS Level 4 and Dictionary

  - NRC Presentation Preparations

  - Review Science Traceability Spreadsheet

  - Identification of High-priority Capabilities

- Walk through presentation with NASA HQ’s (March 1, 2005)

- NRC products delivered to the NRC (March 7, 2005)

- NRC Dialogue (March 16, 2005)

  - A Clear Pathway to Capability Development?

  - Technology Maturity Levels?

  - Metrics for Measuring Technical Maturity Advancement

  - Connection Points to Other Roadmaps?

- Deliver the first draft of Roadmaps

  - Capability Priorities

  - Sub-Capability Roadmaps

  - Integration with Other Roadmaps

- Strategic Roadmap Alignment

- NRC Summary Review

- Final Product Delivery

### 12.A.4.6 SIS Top-Level Assumptions

- Design reference missions and strategic science measurement needs must be driven by the Vision for Space Exploration and the New Age of Exploration (NASA’s Direction for 2005 and Beyond).

  - Supplemental information was obtained (and documented) from science working group interactions, presentations to the Strategic Roadmap Teams and science/engineering technical presentations.

  - Mars Robotic and Human expeditions needs were compiled from the Advanced Mission Studies performed by the Mars Exploration Program Analysis Group (MEPAG).

- Development of realistic Science Instrument and Sensor Roadmaps is dependent upon many CRM team development activities.  Dual membership occurs within the following CRM teams:

  - Advanced Telescopes and Observatories (Ron Polidan)

  - In Situ Resource Utilization (Richard Dissly)

  - Nanotechnology (Carl Stahle)

- Commercial/Academia partnerships are essential to implementing technology solutions required to narrow or close critical capability gaps.

- Roadmap Format:

  - Capability needs are shown in the timeline to be met 3-5 years before mission launch. The target is 3-5 years before Mission launch, where we need to be at TRL 6.

  - Mission timelines were provided by APIO/SMD.

- Roadmap Approach:

  - Science Instruments and Sensors is a broad and diverse roadmapping topic with significant science measurement application challenges.

    - Previous instrument and sensor roadmapping efforts were limited to specific science measurement priorities (Earth Science, Universe, Solar System, etc.).

    - Integration of challenging science measurement needs was a significant driver in determining integrated capability gaps.

  - Extensive participation from past, present and future Principal Investigators is encouraged at public meetings and workshops.

    - Development of science instruments and sensors is a competed, peer-reviewed process where lessons learned can influence future missions.

    - Specific technology implementation strategies are the outcome of the proposal process and not the science instruments and sensors roadmap strategic planning activity.

    - Roadmapping products are subject to a peer review process prior to completion.

  - Sub-Capability elements were prioritized by the degree of cross-cutting applicability to multiple DRMs.

    - Do they enable or enhance scientific discovery?

    - Do they have broad application across instrument and sensor capabilities?

    - Do they meet the needs of multiple exploration mission?

### 12.A.4.7 Microwave Instruments and Sensors (12.1) Assumptions

- Roadmapping Philosophy

  - Highlight capabilities that enable the maximum number of science applications

  - Capability roadmaps are developed at Level 3 (subsystems) to highlight cross-cutting between Level 2 (instrument type) areas

- What Isn’t Covered

  - Non-microwave electromagnetic science instruments

  - Non-science microwave (e.g., Entry, Descent and Landing Navigation)

  - In situ microwave science instruments and sensors

- Mission Drivers

- Astronomy & Astrophysics: Einstein Inflation Probe, SAFIR

- Planetary Science: Jupiter Polar Orbiter/Probes, Neptune Orbiter/Probes, Jupiter Icy Moons Orbiter

- Earth System Science:  Ice Thickness, Global Tropospheric Aerosols, Global Soil Moisture, Ocean Surface Winds, GEO Global Precipation, mmWave GEO Radar, Land deformation InSAR, Ocean Circulation and Eddies, Cloud System Structure, Land deformation repeat pass InSAR

- Connection Points to Other Roadmaps

  - Cross-cutting between Microwave and other groups’ DRMs

- Radiation-hard Processors

- Cryo-coolers

- Cross-cutting between Microwave DRMs

- MMIC RF Technology

- Large Scale ASIC Digital Signal Processing

- Radiation-hard Processors

- Cross-cutting between major science themes

  - Earth Science missions serve as capability test beds for other missions. Examples:

    - Nimbus NEMS&SCAMS => TIROS MSU => DMSP SSM/T

    - SeaSat SAR => Magellan SAR

    - Jason MMICs => JUNO Water/Ammonia Radiometer

    - MLS receivers and spectrometers => Jupiter and Neptune Orbiters

### 12.A.4.8 Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR) (12.2) Assumptions

- Vis-IR near-field sensing, or measurements within planetary atmospheres, covered by in situ

- Important overlaps with telescope technology team (long-baseline systems) in developing advanced interferometers

- Agency will support necessary infrastructure (fabrication, testing, expertise)

- Mission Drivers

- Earth Science:  Black Carbon, Total Column Ozone, GEO Coastal Carbon, L2 Earth Atmosphere Solar Interferometer, LEO Cloud Particle Structure, GEO Lightning Imager

- Planetary Science: Jupiter Polar Orbiter/Probes, Europa Geophysical Explorer, Neptune Orbiter/Probes

- Sun-Solar: MTRAP, Jupiter Polar Orbiter/Probes

- Universe+Earth-like Planets: TPF-C, TPF-I, Einstein Inflation Probe, JDEM, Large Aperture UV-Optical Observatory, SAFIR, Life Finder, Planet Imager/Mapper

- Connection Points to Other Roadmaps

- In situ

- UV-gamma Sensing

- Microwave (sub-mm astrophysics)

- Telescopes

- Nanotechnology

- Infrastructure (fabrication, test, expertise)

### 12.A.4.9 Multi-Spectral Sensing (UV-Gamma) (12.3) Assumptions

- Light-weight, high-resolution, grazing and normal incidence and diffractive optics, plus coatings, are covered by the Advanced Telescopes and Observatories (CRM #4)

- Formation flying capabilities and necessary metrology are covered in CRM #4

- Advanced data handling capabilities are available when needed (high-speed telemetry, data compression, etc.)

- Cooling of large structures (including large-area detectors) and general thermal control covered elsewhere

- Adequate provisions made at the appropriate time for calibration and testing

- Mission Drivers

- Sun-Solar:

  - MTRAP (2020)

  - RAM (2032)

  - SCOPE (2033)

- Universe+Earth-like Planets:

  - Constellation-X (2014)

  - Black Hole Finder Probe (2018)

  - Large UV Observatory (2020)

  - Black Hole Imager (2025)

  - Advanced Compton Telescope (2026)

  - Generation-X (2027)

  - Stellar Imager (2034)

- Connection Points to Other Roadmaps

  - Telescopes and Large Structure

  - Telecommunications

  - Advanced Modeling

  - Infrastructure (fabrication, test, expertise)

### 12.A.4.10 Laser/LIDAR Remote Sensing (12.4) Assumptions

- Receiver optics and infrastructure also addressed by Advanced Telescopes and Observatories Capability Roadmap.

- Agency will support risk reduction activities, including aircraft and ground-based prototype testing.

- Sensors must reach technical maturity 3-5 years before launch.

- Some Earth science sensors have direct planetary applications and vice versa.

- Astrophysical applications using metrology included.

- Tradeoffs:

  - Detection probability:  power versus aperture versus detector sensitivity

  - Spatial coverage:  number of beams versus scanning versus pixelated detectors

- Not covered here:  optical communication, landing range finders, in situ systems.

- Other things that matter:  platform stability, alignment, precise and stable oscillators, precision optics, radiation-hard, low-noise electronics

- Mission Drivers:

  - Earth Science:

    - Calipso/Caliop

    - Tropical Winds

    - Hi Res CO2

    - Advanced Land Cover Change

    - Stratospheric Composition

    - Photosyntnhetic Efficiency

  - Planetary Science:

    - Lunar Reconnaissance Orbiter

    - Europa Geophysical Orbiter

    - Mars High-resolution Spatial Mapper

  - Universe+Earth-like Planets:

    - LISA

    - Big Bang Observer

- Connection Points to Other Roadmaps

  - In situ

  - Telescopes and Structures

  - Data Processing and Storage

  - Advanced Communications

  - Infrastructure (fabrication, test)

  - Nanotechnology

  - Formation Flying

### 12.A.4.11 Direct Sensing of Particles, Fields and Waves (12.5) Assumptions

- Laser transmit/receive telescopes and laser telescope pointing actuator will be covered by the Advanced Telescopes and Observatories (CRM #4)

- Laser development will be covered by Laser/LIDAR sub-team

- Spacecraft disturbance compensation system will be provided separately.

- Development of technology for astrophysics needs to measure gravitational waves will be sufficient for measurements of the gravity field for planetary and earth science applications

- Most Particles and Fields measurement needs can be met with present technology, but planetary environments, the heliosphere and the sun are a dynamic-coupled system that requires distributed measurements. Many future missions will be

multi-spacecraft and/or very limited in payload and cost. Deliberate evolutionary

miniaturization of instruments and electronics is very important to enhance or enable

these future missions.

- Similar miniaturization and reductions in cost are needed for in-situ and remote-sensing instruments and for spacecraft avionics.

- Mission Drivers:

  - Terrestrial:  Ionosphere/Thermosphere Storm Probes (ITSP), Radiation Belt Storm Probes (RBSP), Geospace Electrodynamics Connection (GEC), Magnetospheric Constellation (MC)

  - Planetary: Jupiter Polar Orbiter/Probes (JPOP), Europa Orbiter

  - Heliospheric: Solar Probe (SP), Inner Heliosphere Sentinels  (IHS), Telemachus, Interstellar Probe (ISP),  Heliospheric Imager and Galactic Observer  (HIGO)

  - Astrophysics: Laser Interferometer Space Antenna (LISA), Big Bang Observer (BBO)

- Connection Points to Other Roadmaps

- Laser Remote Sensing

- Advanced Telescopes and Observatories

- Visible-UV Sensing

- In-Situ Instruments

- Nanotechnology

- Infrastructure (fabrication, test, calibration)

### 12.A.4.12 In Situ Instrumentation (12.6) Assumptions

- Vis-IR far-field sensing, or measurements outside of planetary atmospheres, covered by Multi-spectral Imaging sub team

- In-situ measurements of interplanetary plasmas covered in Particles, Fields and Waves sub team

- In-situ sensors for astronaut health and safety are not covered by this group

- General curatorial facilities for sample return will be covered by NASA, including quarantine facilities, independent of this assessment

- Analytical instrumentation and mission-specific environmental maintenance for returned samples are not necessarily provided; this team has not covered capability needs in this area yet

- Development includes the testbeds necessary to successfully implement these instruments in Exploration

- Mission Drivers:

- Mars:  Astrobiology Field Lab, Groundbreaking Mars Sample Return, Deep Drill, Long-Lived Lander Network

- Sample Return: Lunar South Pole-Aitken Basin SR, Comet Surface SR, Comet Cryogenic SR, Asteroid SR, Venus Surface SR, Mercury SR

- Other Planetary: Lunar Seismic Network, Venus In-Situ Explorer, Jupiter Polar Orbiter/Probes, Neptune Orbiter/Probes, Europa Pathfinder Lander, Titan Explorer, Europa Astrobiology Lander, Uranus Orbiter/Probes, Neptune Orbiter w/ Triton Lander

- Connection Points to Other Roadmaps

  - Atmospheric Entry Systems

  - Landing Systems

  - Planetary Surface and Subsurface Access

  - Cryogenic Sample Handling

  - Remote Sensing and Sounding of Surface/Subsurface Composition

  - Nanotechnology

## 12.A.5 Acronyms and Abbreviations

| ACE | Advanced Composition Explorer Mission |
| --- | --- |
| ACS | Advanced Camera for Surveys |
| ACT | Advanced Compton Telescope |
| ADM | Atmospheric Dynamics Mission |
| ADR | Adiabatic Demagnetization Refrigerator |
| AFL | Astrobiology Field Laboratory |
| AFM | Atomic Force Microscope |
| AIRS | Atmospheric Infrared Sounder |
| ALADIN | Atmospheric Laser Doppler Instrument |
| AMSU | Advanced Microwave Sounder Unit |
| APIO | Advanced Planning and Integration Office |
| APL | Applied Physics Laboratory (Johns Hopkins University) |
| APS | Active Pixel Sensor |
| ARC | Ames Research Center |
| ASIC | Application-Specific Integrated Circuit |
| ASTEP | Astrobiology Science and Technology for Exploring Planets |
| ASTID | Astrobiology Science and Technology Instrument Development |
| ATO | Advanced Telescopes and Observatories |
| BATC | Ball Aerospace and Technologies Corporation |
| BBO | Big Bang Observer Mission |
| BHFP | Black Hole Finder Probe Mission |
| BHI | Black Hole Imager Mission |
| BLIP | Background Limited Infrared Photo-detector |
| Bolos | Bolometer Arrays |
| Bolo v. Hetero | Bolometer versus Heterodyne arrays |
| BW | Bandwidth |
| CALIOP | Cloud-Aerosol LIDAR with Orthogonal Polarization |
| CALIPSO | Cloud-Aerosol LIDAR and Infrared Pathfinder Satellite Observation Mission |
| CBS | Capability Breakdown Structure |
| CCD | Charge Coupled Device |
| CMB | Cosmic Microwave Background |
| CMOS | Complementary Metal-Oxide Semi-conductor |
| Con-X | Constellation-X Mission |
| CRISM | Compact Reconnaissance Imaging Spectrometer for Mars |
| CRM | Capability Roadmap |
| Cryo | Cryogenic |
| CSSR | Comet Surface Sample Return Mission |
| cw | continuous wave |
| DBF | Digital Beam Formation |
| DC | Direct Current |
| DCL | NASA GSFC Detector Characterization Laboratory |
| DDL | NASA GSFC Detector Development Laboratory |
| Demo | Demonstration |
| DMSP | Defense Meteorological Satellite Program |
| DoD | Department of Defense |
| DRMs | Design Reference Missions |
| DSP | Digital Signal Processor chip |
| EG | Europa Geophysics Mission |
| EIK | Discrete Power Amplifier |
| EIP | Einstein Inflation Probe Mission |
| ESA | Electronically Scanned Arrays |
| ESMR | Electrically Scanning Microwave Radiometer |
| ESTO | Earth Science Technology Office |
| EUVE | Extreme Ultraviolet Experiment Mission |
| eV | Electron-volt |
| Far IR | Far Infrared |
| FIR | Far Infrared |
| FIRST | Far Infrared and Submillimeter Telescope Mission |
| FOV | Field-of-View |
| FPA | Focal Plane Assembly |
| FPGA | Field-Programmable Gate Array |
| FTS | Fourier Transform Spectrometer |
| FUSE | Far Ultraviolet Spectroscopic Explorer Mission |
| GaAs | Gallium Arsenide |
| GEC | Geospace Electrodynamics Connection Mission |
| Gen X | Generation X Mission |
| GEO | Geosynchronous Orbit |
| GEO Coastal C | GEO Coastal Carbon Mission |
| GEOSAT | Geodetic Satellite Mission |
| GEO Global Precip | GEO Global Precipitation (GGP) Mission |
| GGP | GEO Global Precipitation Mission |
| GHz | Gigahertz |
| GLAS | Geoscience Laser Altimetry System |
| GLAST | Gamma Ray Large Area Space Telescope |
| GPS | Global Positioning System |
| GPS/GNSS | Global Positioning System/Global Navigation Satellite System |
| GRACE | Gravity Recovery and Climate Experiment |
| GRO | Gamma-Ray Observatory Mission |
| GSFC | Goddard Space Flight Center |
| GSM | Global Soil Moisture Mission |
| GTA | Global Tropospheric Aerosols Mission |
| HCIPE | High Capability Instruments |
| HIGO | Heliospheric Imager and Galactic Observer Mission |
| HiRISE | High Resolution Imaging Science Experiment |
| HRes CO2 | High Resolution CO2 |
| HST | Hubble Space Telescope Mission |
| HVPS | High Voltage Power Supply |
| ICESat | Ice, Cloud, and land Elevation Satellite |
| IHS | Inner Heliosphere Sentinels Mission |
| IMAGE | Imager for Magnetopause-to-Aurora Global Exploration Mission |
| InSAR | Interferometric Synthetic Aperture Radar |
| IPS | Integrated Power Systems |
| IR | Infrared |
| IRAC | Infrared Array Camera |
| IRS | Infrared Spectrograph |
| ISP | Interstellar Probe Mission |
| ISRU | In situ Resource Utilization |
| ITSP | Ionosphere/Thermosphere Storm Probes Mission |
| J/Pulse | Joule/Pulse |
| JDEM | Joint Dark Energy Mission |
| JHU | Johns Hopkins University |
| JIMO | Jupiter Icy Moons Orbiter Mission |
| JPL | Jet Propulsion Laboratory |
| JPO | Jupiter Polar Orbiter Mission |
| JPOP | Jupiter Polar Orbiter Probes Mission |
| JWST | James Webb Space Telescope |
| LASCO | Large Angle and Spectrometric Coronagraph Experiment |
| LASER | Light Amplification by Stimulated Emission of Radiation |
| LEO | Low Earth Orbit |
| Leo LFSM | LEO Low Frequency Soil Moisture |
| LF | Life Finder Mission |
| LFF InSAR | L-band Formation Flying InSAR |
| LHP | Loop Heat Pipe |
| LIDAR | Light Detection and Ranging |
| LISA | Laser Interferometer Space Antenna Mission |
| LITE | LIDAR In-Space Technology Experiment |
| LM | Lockheed Martin |
| LOLA | Lunar Orbiter Laser Altimeter |
| LRO | Lunar Reconnaissance Orbiter |
| Lunar SPA-SR | Lunar South Pole-Aitken Basin Sample Return |
| LUVO | Large Aperture Ultraviolet Optical Observatory Mission |
| L2 Interfr | L2 Interferometer |
| Mag Con | Magnetospheric Constellation Mission |
| MARSIS | Mars Advanced Radar for Subsurface and Ionospheric Sounding |
| MC | Magnetospheric Constellation Mission |
| MCM | Multi-Chip Module |
| MCP | Micro-channel Plate |
| MDI/SOI | Michelson Doppler Imager/Solar Oscillations Investigation |
| MDL | NASA JPL Micro-Devices Laboratory |
| MEMS | Micro-Electro-Mechanical Systems |
| MEO | Mid Earth Orbit |
| MEPAG | Mars Exploration Program Analysis Group |
| MER | Mars Exploration Rover |
| MER RAT | Mars Exploration Rover Rock Abrasion Tool |
| MFL | Mars Foundation Laboratory |
| MGS | Mars Global Surveyor Mission |
| MHRSM | Mars High Resolution Spatial Mapper |
| MIDP | Mars Instrument Development Program |
| MIPS | Multiband Imaging Spectrometer for SIRTF |
| MIRI | Mid Infrared Instrument |
| MIT | Massachusetts Institute of Technology |
| mK | millikelvin |
| MLA | Mercury Laser Altimeter |
| MLS | Microwave Limb Sounder |
| MMIC | Monolithic Microwave Integrated Circuit |
| MMS | Magnetospheric Multiscale Mission |
| mmW | millimeter wave |
| mmWave | millimeter wave |
| MODIS | Moderate Resolution Imaging Spectroradiometer |
| MOLA | Mars Orbiter Laser Altimeter |
| Mps | Megabits per second |
| MRO | Mars Reconnaissance Orbiter |
| MSFC | Marshall Space Flight Center |
| MSL | Mars Surface Laboratory |
| MSU | Microwave Sounder Unit |
| MTRAP | Magnetic Transition Region Probe |
| mW | milliwatt |
| NEAR | NLR Near Laser Rangefinder |
| NEMS | Nimbus E Microwave Spectrometer |
| NEP | Noise Equivalent Power |
| NIRCam | Near Infrared Camera |
| NIRSpec | Near Infrared Spectrometer |
| NIST | National Institute of Standards and Technology |
| NLR | NEAR Laser Rangefinder |
| NO | Neptune Orbiter |
| NOAA | National Oceanic and Atmospheric Administration |
| NRC | National Research Council |
| NRO | National Reconnaissance Office |
| NSCAT | NASA Scatterometer |
| OSS | Office of Space Science |
| OSW | Ocean Surface Winds |
| PI | Planet Imager Mission |
| PIDDIP | Planetary Instrument Development and Definition Program |
| ppb | parts per billion |
| PRF | Pulse Repetition Frequency |
| QE | Quantum Efficiency |
| QGG | Quantum Gravity Gradiometer |
| QuickScat | NASA Quick Scatterometer |
| RAM | Reconnection and Microscale Mission |
| RAR | Real Aperture Radar |
| RBSP | Radiation Belt Storm Probes Mission |
| RF | Radio Frequency |
| RHESSI | Ramaty High-Energy Solar Spectrographic Imager |
| rms | root mean square |
| SAFIR | Single Aperture Far Infrared Observatory Mission |
| SAR | Synthetic Aperture Radar |
| SC | Stratospheric Composition Mission |
| S/C | Spacecraft |
| SCAMS | Scanning Microwave Spectrometer |
| SCOPE | Solar Connections Observatory for Planetary Environments Mission |
| SECCHI | Sun Earth Connection Coronal and Heliospheric Investigation |
| SEU | Structure and Evolution of the Universe |
| SI | Stellar Imager Mission |
| SiGe | Silicon Germanium |
| SIR | Shuttle Imaging Radar |
| SIRTF | Space Infrared Telescope Facility Mission (AKA Spitzer Space Telescope) |
| SIS | Science Instruments and Sensors |
| SIT | Sea Ice Thickness Mission |
| SLA | Shuttle Laser Altimeter |
| SMD | Science Mission Directorate |
| SOFIA | Stratospheric Observatory for Infrared Astronomy |
| SOHO | Solar and Heliospheric Observatory Mission |
| SOT | Solar Optical Telescope |
| SP | Solar SIT Probe Mission |
| SPI | Solar Probe Imager |
| SRM | Strategic Roadmap |
| SRTM | Shuttle Radar Topography Mission |
| SSD | Solid State Detector |
| SSED | Solar System Exploration Division |
| SSES | Solar System Exploration Subcommittee |
| SSM/T | Special Sensor Microwave/Temperature |
| STEREO | Solar Terrestrial Relations Observatory Mission |
| SWIR | Shortwave Infrared |
| ( | transmissivity |
| TDI | Time Delay and Integration |
| TES | Thermal Emission Spectrometer (Mars Global Surveyor) |
| TES | Tropospheric Emission Spectrometer (Aura) |
| THz | Terahertz |
| THEMIS | The History of Events and Macroscale Interactions During Substorms |
| TIMED | Thermosphere Ionosphere Mesosphere Energetics and Dynamics Mission |
| TIPS | Tera Instruction Per Second |
| TIROS | Television Infrared Operational Satellite |
| TOF | Time-of-Flight |
| TOPEX | Topography Experiment |
| TPF-C | Terrestrial Planet Finder-Coronagraph Mission |
| TPF-I | Terrestrial Planet Finder-Interferometer Mission |
| T/R | Transmitter/Receiver |
| Tx/Rx | Transmitter/Receiver |
| TRL | Technology Readiness Level |
| TRMM | Tropical Rainfall Measuring Mission |
| Tropical ITM | Tropical ITM Couplet Mission |
| UM | University of Michigan |
| UV | Ultraviolet |
| UW | University of Wisconsin |
| VAP | Venus Aeronomy Probe |
| VHF | Very High Frequency |
| VIMS | Visible and Infrared Mapping Spectrometer |
| Vis | Visible |
| VISE | Venus In Situ Experiment (Explorer) Mission |
| WMAP | Wilkinson Microwave Anisotropy Probe |

# Text boxes

Figure 12.6b

In-Situ Instrumentation Far Term Capability Roadmap

7/15/05                                                             SIS Capability Portfolio                                                        Page 42

7/15/05                                                        SIS Capability Portfolio                                                        Page 41

Figure 12.6a

In-Situ Instrumentation Near Term Capability Roadmap

Figure 12.5a

Direct Sensing of Particles, Fields and Waves Near Term Capability Roadmap

7/15/05                                                           SIS Capability Portfolio                                                    Page 35

Figure 12.5b

Direct Sensing of Particles, Fields and Waves Far Term Capability Roadmap

7/15/05                                                            SIS Capability Portfolio                                                 Page 36

Figure 12.5a

Direct Sensing of Particles, Fields and Waves Near Term Capability Roadmap

Figure 12.5a

Direct Sensing of Particles, Fields and Waves Near Term Capability Roadmap

Figure 12.4a

Laser/LIDAR Remote Sensing Near Term Capability Roadmap

7/15/05                                                         SIS Capability Portfolio                                                       Page 29

Figure 12.4b

Laser/LIDAR Remote Sensing Far Term Capability Roadmap

7/15/05                                                        SIS Capability Portfolio                                                     Page 30

Figure 12.3a

Multi-Spectral Sensing (UV-Gamma) Near Term Capability Roadmap

7/15/05                                                              SIS Capability Portfolio                                                   Page 23

Figure 12.3b

Multi-Spectral Sensing (UV-Gamma) Far Term Capability Roadmap

7/15/05                                                          SIS Capability Portfolio                                                       Page 24

Figure 12.2a

Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR) Near Term Capability Roadmap

7/15/05                                                           SIS Capability Portfolio                                                     Page 17

Figure 12.2b

Multi-Spectral Imaging/Spectroscopy (Vis-IR-FIR) Far Term Capability Roadmap

7/15/05                                                                SIS Capability Portfolio                                                     Page 18

Figure 12.1a

Microwave Instruments and Sensors Near Term Capability Roadmap

7/15/05                                                                SIS Capability Portfolio                                                        Page 11

Figure 12.1b

Microwave Instruments and Sensors Far Term Capability Roadmap

7/15/05                                                               SIS Capability Portfolio                                                   Page 12