MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A04175 | In-Flight Anomaly Number -- | Contractor Report Number S-054 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title BOLT BREAKAGE, LO INTERTANK TO LH2 TANK ATTACHMENT |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# ET-6 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE BOLT | PART# 26L2-9 | SER/LOT# N/A | MANUFACTURER N/A |
| Test/Operation L - FLD | Prevailing Condtion -- | F / U F | Fail Mode -- | Cause -- |
| System STRUCTURAL | Defect DC - BROKEN | Material -- | Work Contact J. FINCHER | Fail Date 12/16/1981 |
| Received at MSFC 01/14/1982 | Date Isolated -- | FMEA Reference 1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom -- | Time Cycle -- |
| Effectivity Text LWT-1 AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 05/11/1982 | Defer Date -- | Add Date -- | R/C Codes 1 - DES -- -- |
| Assignee |
| Design J. NICKOLS | Chief Engineer -- | S & MA D. NEWMAN | Project M. PESSIN | Project MGR -- |
| Approval |
| Design J. NICKOLS | Chief Engineer -- | S & MA D. NEWMAN | Project J. ODOM | Project MGR -- |
| PAC Assignee M. GLASS | PAC Review Complete -- | MSFC Closure Date 08/04/1982 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: DURING THE PROCESS OF SECURING ET-6 INTERTANK TO LH2 TANK. A 26L2-9 (9/16") BOLT SHEARED JUST PRIOR TO OBTAINING THE REQ'D TORQUE OF 240 FT/LBS. THE BOLT SHEAR OCCURRED IN THE THREADED AREA ADJACENT TO THE BOLT SHANK |
| Contractor Investigation/Resolution CAUSE - INSUFFICIENT NO. OF WASHERS INSTALLED UNDER NUT END OF BOLT WHICH CAUSED SHANKING CONDITION & OVERLOAD OF BOLT. 5/11/82 RESOLUTION - IT WAS OBSERVED THAT AN INSUFFICIENT NO. OF WASHERS WERE USED UNDER THE NUT. THIS PRODUCED A CONDITION WHERE THE NUT ENGAGED IMPERFECT THREADS NEAR THE BOLT SHANK, THEREBY INCREASING BOLT TORSION & SHEARING THE BOLT. FAILURE ANALY SHOWED THE BOLT IS CORRECT MTR (A268) OF PROPER ROCKWELL HARDNESS (C38-40, WITH NO OTHER ABNORMALITITES. ALL BOLTS IN THE SPLICE WHEN FAILURE OCCURRED WERE REMOVED & SUBJECTED TO FAILURE ANALY ALL EXCEEDED NEW BOLT REQMNTS. ALL TORQUE WRENCHES WERE TESTED FOR ACCURACY & WERE WITHIN CALIBRATED VALVES. UPON REINSTALLATION OF NEW BOLT IN ET-6 THREAD PROTRUSION MSRMNTS WERE MADE TO ASSURE BOLTS WERE NOT BEING SHANKED (REF MARS T-49544 MARS .182 IN.). RECURRENCE CONTROL - 5/11/82 - REQUESTED R/C BACK-UP INFO MMC. EFFECTIVITY - ET-3,4,5 - ENGR'G ANALY PROVED WORST CASE MAX. LOAD ON EACH BOLT OCCURS DURING TORQUE OPERATION DUE TO CONTRIBUTING TORSION LOAD OF TORQUE ON BOLT, ALSO ANALY SHOWS SEVERAL BOLTS MAY FAIL WITHOUT STRUCTURAL SEPARATION (CHART 1) THEREFORE ET-3,4,5 OK FOR FLT 'AS IS'. ET-6 - ALL BOLTS WERE REPLACED & A MSRMNT WAS MADE TO ASSURE THREAD PROTRUSION IS LESS THAN .182 IN.& BOLTS ARE NOT BEING SHANKED. ALSO ABOVE ENGR ANALY IS APPLICABLE TO ET-6. LWT-1 & SUBS - ENGR ANALY IS BEING MADE TO RE-EVALUATE ALL THRU HOLE APPLICATIONS TO VERIFY BOLT LENGTH & APPLICABLE TORQUE VALVES. 5/13/82 - REQUESTED R.C. BACK-UP DATA (CHANGE SUMMARY J30671) PER TELECON. 7/1/82 - REC'D CAPS ADDENDUM. LWT-1 & UP RECURRENCE OF PROB IS PREVENTED BY REVISING TORQUE REQMNTS - REV "A" FLAG 3, SHT 2, OF DWG 80911000000 REDUCES TORQUE VALVE ON FASTENERS FLAG 14, SHT 2 ESTABLISHES REQMNT TO MEASURE EXTENSION PAST NUT AFTER FINAL TORQUE HAS BEEN ACHIEVED. REF ECP J30671. 7/12/82 - CLOSURE DISTRIBUTED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A04175 | IFA# -- | Contractor RPT# S-054 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# -- | Asmnt Part Name -- | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD -- | CAUSE CD -- | FAIL MODE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |