### Biological Upgrading of Heavy Oil for Viscosity Reduction

William T. Stringfellow
Biological Processing Laboraotory
Lawrence Berkeley National Laboratory
Berkeley, CA
wstringfellow@lbl.gov

#### August 29, 2001

### Introduction

The United States petroleum industry is increasingly dependent on heavy crude oil to meet the domestic demand for gasoline and distillate fuels.  Owing to their high viscosity, heavy oils are more expensive to transport and process than less viscous oils.  It has been proposed that “bioprocessing” may offer an economical approach for treating heavy oil at the wellhead, before pipeline transport.

Biocatalytic viscosity reduction (bioprocessing) uses bacteria to partially transform less valuable crude oil components to surface-active compounds (alcohols and carboxylic acids) that reduce crude oil viscosity.  In this research, we have targeted the terminal oxidation of alkanes to alcohols as a specific mechanism for development.  Research conducted at Texaco has demonstrated the efficacy of linear alcohols in reducing crude oil viscosity.  Biological conversion of alkanes to alcohols is carried out by alkane monooxygenase, an enzyme found in bacteria able to grow on alkanes.  The development of biocatalysts that convert alkanes to alcohols has application both in refining and in bulk chemical manufacturing and is therefore an attractive target for research.

A major challenge to implementing crude oil bioprocessing is to develop and control biocatalytic agents so that they target specific alkanes in complex mixtures.   We have defined the specific challenge of being able to oxidize alkanes of C8 and above without oxidizing alkanes of C7 or less.  We are further interested in understanding the difference between bacteria that oxidize iso-pentane from those that do not.  Iso-pentane is a major component of gasoline and is highly valued in crude oil.

For biocatalytic viscosity reduction to be economical, the process will have to be operated under non-sterile conditions using whole-cell biocatalysts.  Non-sterile operation precludes the use of genetically engineered organisms and requires that the process be controlled to maintain desirable biocatalytic agents and favorable kinetics in the presence of competing bacteria.  A successful process will depend on a complete understanding of bacterial alkane oxidation, on the physiologic, genetic, and kinetic level.

The objective of this research was to evaluate diversity among alkane monooxygenases and to develop methods for selecting and evaluating biocatalytic agents for use in viscosity reduction and chemical manufacture.  We investigated differences between well-characterized alkane oxidizing bacteria and novel environmental isolates.  Our study has shown that there is significant variation among alkane oxidizing microorganisms in terms of their phylogeny, physiology, genetics, substrate specificity, and alkane oxidation kinetics.   Some alkane oxidizing microorganisms are considerably different from well-characterized strains and deserve further study.  As a result of this research, we have developed methods for screening and evaluating bacteria as potential biocatalytic agents.  We have identified microorganisms that have significantly different genetic profiles than known alkane oxidizing organisms and selected promising bacterial strains for further development.

### Research statement

A controlled process under non-sterile conditions will require a thorough understanding of both the substrate specificity and the kinetic activity of proposed biocatalysts.  Understanding of the enzymatic diversity of alkane oxidizing bacteria is the first step in the selection and application of bacterial catalytic agents (biocatalysts) for the processing of specific alkanes in complex mixtures.

### Research approach

In this research, we isolated bacteria from petroleum-contaminated environments based on their ability to utilize octane as a growth substrate.  We compared our bacteria to a well-characterized alkane degrading bacteria, Pseudomonas putida (oleovorans) GPo1 (kindly provided to us by Bernard Witholt of the ETH, Zurich).  Strain GPo1 contains a well-characterized alkane monooxygenase enzyme (AlkB) that oxidizes linear alkanes to 1-alcohols (van Beilen et al. 1994).  The alkB gene codes for AlkB enzyme (van Beilen et al. 2001).  GPo1 is a benchmark organism, and most of what is known about the genetics and enzymology of alkane oxidation has been discovered using AlkB system or closely related proteins (Marin et al. 2001).

### Research results

Bacterial isolation and phylogenic analysis

Isolation of microorganisms containing an appropriate enzyme system is the first step in the development of a biocatalyst.  Bacteria were enriched from petroleum contaminated environments using octane as a sole carbon and energy source.  Bacteria were isolated on Luria-Bertani agar in an octane atmosphere (LB-OCT).  Isolated bacteria were sorted according to source of isolation and colony type on LB-OCT.  Specific strains were selected as ‘type-strains’ for each colony type.  Fatty acid methyl ester (FAME) and 16s ribosomal-DNA (rDNA) analyses were used to determine the phylogenic category of the type-strains.

Thirty strains from three different alkane contaminated environments were isolated for testing.  Environmental isolates were compared to the well-characterized bacterial culture strain GPo1 and a negative control strain GPo12 (Smits et al. 1999).  Results from twenty-seven strains and the controls are included in this report. The bacteria were sorted into 15 groups based on their colony morphology or other characteristics.  From each group, one strain was selected as the “type-strain” and characterized by FAME and 16s rDNA analysis (Table 1).  The type-strains were subject to the most complete analysis.  Except where otherwise noted, the results gathered with the type-strains were found to be representative of their entire group.

The majority of organisms isolated in this study were Gram positive actinomycetes bacteria (family Actinomycetaceae).  This group includes Rhodococcus, Nocardioides, Nocardia, Mycobacterium, and Ochrobactrum.   These bacteria are well known for their ability to grown on alkanes and produce surfactants (Hommel 1990).  However, the alkane oxidase activity of actinomycetes has not been extensively studied and the isolation of new alkane oxidizing strains in this group presents opportunities for the development of novel biocatalysts.

Substrate specificity

The substrate range of all bacteria was tested using a plate assay.  Results from the type-strains are presented in Table 2.  Bacteria were plated on a mineral salts (SSC) agar and placed in chambers containing alkane vapors.  Growth of the bacteria on alkanes was evaluated after seven, fourteen, and twenty-one days and scored on a scale of zero to four, with four being the most abundant growth.  Alkane oxidase activity was also confirmed using a respirometric assay (Stringfellow et. al. 2001a, Stringfellow et al. 2001b).

Most of the organisms isolated were able to grow on and oxidize a wide variety of alkanes (Table 2).  Rhodococcus globerulus OT15DY, Nocardioides simplex OT13D1, and Rhodococcus globerulus OT18A were able to grown on all alkanes tested.  Nocardia nova OT32AA and Mycobacterium fortuitum OT32DG were able to transform all the alkanes except iso-pentane.  Bacterial strain OT32AB (not yet identified) was limited to the metabolism of alkanes of C10 or less.  The reference strain, Pseudomonas putida GPo1, was not able to grow on iso-pentane or alkanes above C10 in length.  Alcaligenes xylosoxydans OT6A demonstrated an unusual metabolic pattern, exhibiting poor growth on only on three of the hydrocarbons tested.  These results suggest that there is a significant diversity in alkane metabolizing ability among bacteria.  This diversity offers opportunities for the development of catalysts targeted toward specific alkanes, if the mechanism of specificity can be better understood.

Genetic evaluation

As part of our biocatalyst development, the type-strains were tested for the presence of genes that were homologous with AlkB type monooxygenases (van Beilen et al. 2001, Marin et al. 2001).  The potential biocatalytic agents were screened for the presence of the alkB gene using a non-specific primer set developed to probe for alkB in diverse organisms (Smits et al. 1999).  Homology with alkB of strain GPo1 was indicated by the presence of a PCR product that was approximately 550 bp in size.

All strains that were negative for alkane oxidation were negative for the presence of alkB (Table 3).  Four of the seven alkane metabolizing strains were positive for the presence of an alkB gene of the same size as the positive control (GPo1).  OT6A had some homology with alkB, but on a smaller PCR product (approximately 220 bp).  Two strains, OT32AA and OT32DG, did not demonstrate homology with alkB using these primer sets (Table 3).  There was no clear correlation between homology with alkB and biocatalyst substrate specificity.  These results suggest that there are alkane oxidizing enzymes that are not AlkB type enzymes in some microorganisms.   Further investigation will determine if these strains contain truly novel enzymes.

Kinetic evaluation

The development and application of biocatalysis for alkane oxidation requires a complete understanding of the kinetic properties of the catalysts.  Alkane oxidation rate as a function of alkane concentration was measured using mixed and pure cultures.  From these measurements, the kinetic parameters Km and Vmax were estimated by fitting data to the Henri-Michaelis-Menton equation (Segal 1975).  Results from measurements made with octane for the type-strains are presented in Table 4.  These results demonstrate a variability among biocatalysts that is not apparent from the substrate specificity assay.

Kinetic measurements are being made for a full range of alkanes that will allow the prediction of product formation in different mixtures of alkanes.  Mixed cultures were tested for their ability to oxidize a variety of alkanes.  Competitive inhibition models (Segal 1975) were used to predict the fate of iso-pentane in the presence of other alkanes, such as octane.   The higher affinity of an alkane oxidase for octane than iso-pentane suggested that it would be possible to selectively oxidize octane in the presence of iso-pentane (Stringfellow 2001).

### Research summary and conclusion

The alkane oxidizing bacteria isolated as part of this study were compared to the well-characterized AlkB system of Pseudomonas putida GPo1 for differences and similarities in genetics, kinetics, substrate specificity, and phylogeny.  This study has shown that there is considerable diversity among alkane oxidizing bacteria and opportunities for the development of novel biocatalysts.  Five bacterial strains characterized in this study have been selected for further development.  The bacteria are considered to have potential as biocatalytic agents due to their substrate specificity, kinetic properties, or their probability of harboring novel enzyme systems.

As currently conceptualized, crude oil bioprocessing will be operated under non-sterile conditions and the directed oxidation of long-chain alkanes will be effected by a combination of biocatalyst selection and engineering controls.  The results of substrate specificity and kinetic analysis suggest that there is significant potential for the development of a biocatalytic process that can oxidize less valuable, longer chain alkanes, without damaging valuable, gasoline range alkanes.  Further research is needed to better characterize the action of biocatalysts in alkane mixtures.  The factors that determine substrate specificity need to be better understood and new methods of biological process control need to be developed before bioprocessing can be implemented.

### References

Hommel, R. K. 1990. Formation and physiological role of biosurfactants produced by hydrocarbon-utilizing microorganisms: biosurfactants in hydrocarbon utilization. Biodegradation 1: 107-19.

Marin, M. M., T. H. M. Smits, J. B. Van Beilen, and F. Rojo. 2001.  The alkane hydroxylase gene of Burkholderia cepacia RR10 is under catabolite repression control.  J. Bacteriology 183: 14: 4202-9.

Segel, I. H. 1975.  Enzyme Kinetics: Behavior and Analysis of Rapid Equilibrium and Steady-State Enzyme Systems.  New York: John Wiley and Sons.

Smits, T. H. M., M. Rothlisberger, B. Witholt, and J. B. Van Beilen. 1999.  Molecular screening for alkane hydroxylase genes in Gram-negative and Gram-positive strains. Environ. Microbiol. 1: 4: 307-17.

Stringfellow, W. T.  2001.  Evaluation of bacterial biocatalysts for terminal alkane oxidation.  Abstracts of the 221st American Chemical Society National Meeting, San Diego, CA, April 1 – 5.

Stringfellow, W. T., S. Smriga, K. C. Oh, and T. Letain.  2001a.  Evaluating novel alkane-oxidizing bacteria for the biological up grading of crude oil.  Abstracts of the 101st Annual Meeting of the American Society for Microbiology, Orlando, FL, May 20 - 24.

Stringfellow, W. T., S. Smriga, K. C. Oh, and T. Letain.  2001b.  Evaluation of metabolic diversity among potential bacterial catalysts.  Twenty-Third Symposium on Biotechnology for Fuels and Chemicals, Breckenridge, CO, May 6 – 9.

Van Beilen, J. B., J. Kingma, and B. Witholt. 1994.  Substrate specificity of the alkane hydroxylase system of Pseudomonas oleovorans GPo1. Enz. Microbial Technology 16: 10: 904-11.

Van Beilen, J. B., S. Panke, S. Lucchini, A. G. Franchini, M. Rothlisberger, and B. Witholt. 2001.  Analysis of Pseudomonas putida alkane-degradation gene clusters and flanking insertion sequences: evolution and regulation of the alk genes.  Microbiology-SGM 147: PT6: 1621-30.

Table 1. Phylogenic analysis of potential biocatalytic agents.  Strains were selected for further analysis based on their diversity.

| Strain Name | Strain Category | Colony Description (LB-OCT.) | FAME | 16s rDNA |
| --- | --- | --- | --- | --- |
| OT15DY * | 1 | circular, cream, entire, convex | Rhodococcus erythropolis (0.696) | Rhodococcus globerulus |
| OT15DY1 | 1 | circular, cream, entire, convex |  |  |
| OT15DY2 | 1 | circular, cream, entire, convex |  |  |
| OT16 | 1 | circular, cream, entire, convex |  |  |
| OT16AD1 | 1 | circular, cream, entire, convex |  |  |
| OT16B | 1 | circular, cream, entire, convex | Rhodococcus erythropolis (0.666) |  |
| OT16BD1 | 1 | circular, cream, entire, convex |  |  |
| OT17 | 1 | circular, cream, entire, convex |  |  |
| OT18H2 | 1 | circular, cream, entire, convex |  |  |
| OT18HD2 | 1 | circular, cream, entire, convex |  |  |
| OT25BD1 | 1 | circular, cream, entire, convex |  | Rhodococcus globerulus |
| OT25BD2 | 1 | circular, cream, entire, convex |  | Rhodococcus globerulus |
| OT2A | 1 | circular, cream, entire, convex |  |  |
| OT6A * | 2 | circular, blue halo/diffuse cream center, entire | Alcaligenes xylosoxydans (0.827) |  |
| OT2B | 2 | circular, blue halo/diffuse cream center, entire |  |  |
| OT6B * | 3 | circular, pink, entire, pinpoint, pulvinate |  | Staphylococcus saprophyticus |
| OT33A | 3 | circular, pink, entire, pinpoint, pulvinate |  |  |
| OT33B | 3 | circular, pink, entire, pinpoint, pulvinate |  |  |
| OT13D1 * | 4 | circular, beige, undulate, flat | no match | Nocardioides simplex |
| OT26A * | 5 | punctiform, light cream, irregular, raised | Streptoverticillium sp. (0.392) | Streptomyces sp. |
| OT18A * | 6 | circular, blue halo/cream center, filamentous, convex | Rhodococcus erythropolis (0.763) | Rhodococcus globerulus |
| OT18AD1 | 6 | circular, blue halo/cream center, filamentous, convex |  |  |
| OT32AA * | 7 | circular, light orange, entire, convex, pinpoint | Nocardia sp. (0.336) | Nocardia nova |
| OT32DO | 7 | circular, light orange, entire, convex, pinpoint |  |  |
| OT32DG * | 8 | punctiform, white, entire, flat, small pinpoint | Rhodococcus equi (0.521) | Mycobacterium fortuitum |
| OT18F * | 9 | circular, blue halo/solid cream center, entire, convex | Ochrobactrum sp. (0.568) | Ochrobactrum anthropi |
| OT32AB * | 12 | beige, whitish small round |  |  |
| GPo1 † | 10 | circular, beige, entire, diffused green pigment | Pseudomonas sp. (0.648) | Pseudomonas pseudoalcaligenes |
| GPo12 ‡ | 10 | circular, beige, entire, diffused green pigment |  | Pseudomonas pseudoalcaligenes |

* Type-strain for strain category, † Positive control, ‡ Negative control

Table 2: Substrate specificity of potential biocatalytic agents.  Results demonstrate difference among alkane oxidizing bacteria that is important to their utility as biocatalytic agents.

| Strain Name | Iso-pentane | Pentane | Hexane | Octane | Decane | Dodecane | Tetradecane | Pentadecane | Hexadecane |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| OT15DY | 3 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 |
| OT6A | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |
| OT6B | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| OT13D1 | 2 | 2 | 1 | 2 | 2 | 3 | 2 | 2 | 2 |
| OT26A | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| OT18A | 2 | 2 | 2 | 3 | 2 | 3 | 3 | 3 | 2 |
| OT32AA | 0 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 |
| OT32DG | 0 | 2 | 0 | 3 | 3 | 3 | 3 | 3 | 3 |
| OT18F | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| OT32AB | 1 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 |
| GPo1 | 0 | 3 | 2 | 3 | 2 | 3 | 0 | 0 | 0 |
| GPo12 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

0 = absolutely no growth, 1 = no significant growth away from primary streak; micro-colony, 2 = very faint colony formation, 3 = very definitive growth, 4 = maximum growth on plate

Table 3: Strain homology with alkB, a well-characterized gene coding alkane monooxygenase.  Four different primer sets yielded the same results.  Homology with known alkB genes did not correlate with hydrocarbon utilization patterns.  Alkane oxidizing strains that do not have homology with alkB may harbor a novel mechanism for alkane oxidation.

| Strain Name | alkB (TS2S/deg1RE) | alkB (TS2S/deg1RE2) | alkB (TS2Smod/deg1RE) | alkB (TS2Smod/deg1RE2) | Hydrocarbon utilization pattern |
| --- | --- | --- | --- | --- | --- |
| OT15DY | yes | yes | yes | yes | All HC |
| OT6A | no | no | no | no | C8, C10, C15 |
| OT6B | no |  |  |  | None |
| OT13D1 | yes | yes | yes | yes | All HC |
| OT26A | no |  |  |  | None |
| OT18A | yes | yes | yes | yes | All HC |
| OT32AA | no |  |  |  | n-C5 - C16 |
| OT32DG | no |  |  |  | n-C5 - C16 |
| OT18F | no | no | no | no | None |
| OT32AB |  |  |  |  | n-C5 - C12 |
| GPo1 | yes | yes | yes | yes | n-C5 - C12 |
| GPo12 | no | no | no | no | None |

Table 4: Kinetic evaluation of potential biocatalytic agents. Results demonstrate that biocatalysts have different levels of alkane monooxygenase expression (Vmax) and harbor enzymes with different affinities for the oxidation of octane (Km).  Understanding kinetic differences between biocatalysts is important to the development of an engineered process.

| Strain Name | Vmax for octane ((moles O2/min/g biomass) | Km for octane ((M) |
| --- | --- | --- |
| OT15DY | 30 | 1.28 |
| OT6A | 32 | 2.14 |
| OT13D1 | 13 | 0.43 |
| OT18A | 82 | 2.76 |
| OT32AA | 29 | 0.74 |
| OT32DG | 9 | 0.81 |
| GPo1 | 28 | 1.57 |