BARROW METEOROLOGICAL TOWER

DAILY PM PROCEDURE

This document describes the daily PM procedures to be conducted at the NSA C1 Barrow site.

The following items that are not included in the daily rounds forms or on the LoggerNet RTMC Overview screen are to be verified.  Any discrepancy will be noted in the comments section of any of the Daily Rounds forms.

- Verify operation of the computer by checking the time and making sure it is correct and changing.  This can be done by use of the computer’s task bar or any of the LoggerNet RTMC screens that have a date and time display.

- Verify that LoggerNet is running.  This can be done by verifying that the LoggerNet task bar is up and available or verifying the RTMC screens are live and updating.

The below images have circles and numerals on them.  The numerals located on the Daily Rounds form have a corresponding numeral on the RTMC Overview screen.  These corresponding numerals on the RTMC highlight where information is found to answer the questions on the Daily Rounds form.  The corresponding numerals work for all portions of the Daily Rounds form except for the Ground Visual Checks and the Monthly CMH Autobalance Reading sections.  The Ground Visual Checks are accomplished by visually checking the tower, and the Autobalance Reading is accomplished by physically opening the CMH and reading the values off the dial.  See the Met Tower Users Manual for procedures on obtaining an Autobalance Reading.