This document was provided by EarthSat Corporation along with the GeoCover data.

Land Cover for Afghanistan and Surrounding Area

Draft Proposal

Earth Satellite Corporation (EarthSat) is pleased to provide this proposal to provide land cover for Afghanistan and surrounding area.  This product will be similar to EarthSat’s GeoCover LC product that is provided to NIMA, except this product will achieve greater accuracy in the landcover classification and will use additional landcover classes for developed and barren areas. This product will be referenced as EarthSat’s Customized GeoCover LC product.  This landcover product will be derived from 122 scenes of Landsat ETM data.  The landcover will be derived from the 30-meter resolution multispectral imagery.  The 15-meter panchromatic imagery will be used as collateral information to assist in creating various landcover classes, especially the two developed area classes.

This proposal describes (1) the study area,  (2) the Landsat ETM scenes to be used, (3) the landcover categories proposed, (4) the raster products to be delivered, (5) optional vector landcover products that can be provided, (6) ground truth data that will be required, (7) client and EarthSat’s data rights, (8) proposed delivery schedule, and (9) cost.

Study Area

EarthSat’s Customized LC products will be produced for the study area as shown in Figure 1.  It should be noted that EarthSat’s has a separate proposal to orthorectify the 122 Landsat ETM scenes required to cover this study and the cost of the imagery and the orthorectification of this imagery is not included in this study area.

The approximate study area extend is from 27.5 degrees latitude north to 38.75 degrees latitude north and from 59.5 degrees longitude east to 75.5 degrees longitude east.   The Landsat ETM imagery will be orthorectified to UTM, Zone 42, WGS84.  The extent of the study area in UTMs will be from  -500000 E to 1300000 E and from 2950000 N to 4450000 N, resulting in a study area that is 1,800 km wide (east/west) by 1,500 km high (north/south).  The orthorectified imagery will be provided as 128 tiles (in UTM) with each tile being 150 km wide (east/west) by 150 km high (north/south).  This size was chosen to ensure that a single tile of orthorectified Landsat ETM imagery would fit on a single CD.  Up to 10 tiles of landcover data will fit on each CD.

Figure 1. Study area for EarthSat’s Customized GeoCover LC product for Afghanistan and surrounding area.

Landsat ETM Scenes

Table 1 provides a list of the proposed Landsat TM scenes to be used in this study.  Figure 2 shows this distribution of these scenes by time.

Table 1. List of the proposed 104 scenes to be used for creating the EarthSat’s Customized GeoCover LC product for Afghanistan and surrounding area.

| Number | Path/Row | Date | % Cloud Cover |
| --- | --- | --- | --- |
| 1 | P147R040 | 24-May-00 | 0 |
| 2 | P147R041 | 18-May-01 | 0 |
| 3 | P148R036 | 18-May-01 | 0 |
| 4 | P148R037 | 13-Apr-00 | 16 |
| 5 | P148R038 | 15-May-00 | 3 |
| 6 | P148R039 | 2-May-01 | 0 |
| 7 | P148R040 | 2-May-01 | 0 |
| 8 | P148R041 | 2-May-01 | 0 |
| 9 | P149R033 | 7-Apr-01 | 3 |
| 10 | P149R034 | 7-Apr-01 | 3 |
| 11 | P149R035 | 6-May-00 | 2 |
| 12 | P149R036 | 7-Apr-01 | 0 |
| 13 | P149R037 | 7-Apr-01 | 0 |
| 14 | P149R038 | 7-Apr-01 | 0 |
| 15 | P149R039 | 25-May-01 | 0 |
| 16 | P149R040 | 7-Apr-01 | 0 |
| 17 | P149R041 | 7-Apr-01 | 0 |
| 18 | P150R033 | 30-Apr-01 | 1 |
| 19 | P150R034 | 30-Apr-01 | 2 |
| 20 | P150R035 | 11-Apr-00 | 0 |
| 21 | P150R036 | 11-Apr-00 | 0 |
| 22 | P150R037 | 30-Apr-01 | 0 |
| 23 | P150R038 | 30-Apr-01 | 0 |
| 24 | P150R039 | 30-Apr-01 | 0 |
| 25 | P150R040 | 30-Apr-01 | 0 |
| 26 | P150R041 | 30-Apr-01 | 0 |
| 27 | P151R033 | 24-Aug-00 | 0 |
| 28 | P151R034 | 23-May-01 | 3 |
| 29 | P151R035 | 23-May-01 | 0 |
| 30 | P151R036 | 21-Apr-01 | 0 |
| 31 | P151R037 | 23-May-01 | 0 |
| 32 | P151R038 | 23-May-01 | 0 |
| 33 | P151R039 | 23-May-01 | 0 |
| 34 | P151R040 | 23-May-01 | 0 |
| 35 | P151R041 | 23-May-01 | 0 |
| 36 | P152R033 | 2-Aug-01 | 0 |
| 37 | P152R034 | 2-Aug-01 | 0 |
| 38 | P152R035 | 2-Aug-01 | 0 |
| 39 | P152R036 | 30-May-01 | 0 |
| 40 | P152R037 | 28-Apr-01 | 0 |
| 41 | P152R038 | 28-Apr-01 | 0 |
| 42 | P152R039 | 28-Apr-01 | 0 |
| 43 | P152R040 | 28-Apr-01 | 0 |
| 44 | P152R041 | 28-Apr-01 | 0 |
| 45 | P153R033 | 8-Jul-01 | 0 |
| 46 | P153R034 | 8-Jul-01 | 0 |
| 47 | P153R035 | 8-Jul-01 | 0 |
| 48 | P153R036 | 25-Aug-01 | 0 |
| 49 | P153R037 | 25-Aug-01 | 0 |
| 50 | P153R038 | 3-Apr-01 | 0 |
| 51 | P153R039 | 3-Apr-01 | 0 |
| 52 | P153R040 | 3-Apr-01 | 0 |
| 53 | P153R041 | 3-Apr-01 | 0 |
| 54 | P154R033 | 31-Jul-01 | 0 |
| 55 | P154R034 | 31-Jul-01 | 0 |
| 56 | P154R035 | 29-Jun-01 | 0 |
| 57 | P154R036 | 29-Jun-01 | 0 |
| 58 | P154R037 | 29-Jun-01 | 0 |
| 59 | P154R038 | 29-Jun-01 | 0 |
| 60 | P154R039 | 29-Jun-01 | 0 |
| 61 | P154R040 | 29-Jun-01 | 0 |
| 62 | P154R041 | 12-May-01 | 0 |
| 63 | P155R033 | 3-May-01 | 0 |
| 64 | P155R034 | 3-May-01 | 0 |
| 65 | P155R035 | 3-May-01 | 0 |
| 66 | P155R036 | 3-May-01 | 0 |
| 67 | P155R037 | 3-May-01 | 0 |
| 68 | P155R038 | 3-May-01 | 0 |
| 69 | P155R039 | 3-May-01 | 0 |
| 70 | P155R040 | 3-May-01 | 0 |
| 71 | P155R041 | 3-May-01 | 0 |
| 72 | P156R033 | 27-Jun-01 | 0 |
| 73 | P156R034 | 27-Jun-01 | 0 |
| 74 | P156R035 | 27-Jun-01 | 0 |
| 75 | P156R036 | 27-Jun-01 | 0 |
| 76 | P156R037 | 27-Jun-01 | 0 |
| 77 | P156R038 | 10-May-01 | 0 |
| 78 | P156R039 | 10-May-01 | 0 |
| 79 | P156R040 | 10-May-01 | 0 |
| 80 | P156R041 | 10-May-01 | 0 |
| 81 | P157R033 | 14-May-00 | 0 |
| 82 | P157R034 | 17-May-01 | 0 |
| 83 | P157R035 | 17-May-01 | 0 |
| 84 | P157R036 | 17-May-01 | 0 |
| 85 | P157R037 | 17-May-01 | 0 |
| 86 | P157R038 | 17-May-01 | 0 |
| 87 | P157R039 | 30-Mar-01 | 0 |
| 88 | P157R040 | 1-May-01 | 0 |
| 89 | P157R041 | 1-May-01 | 0 |
| 90 | P158R033 | 3-Apr-00 | 0 |
| 91 | P158R034 | 11-Jul-01 | 0 |
| 92 | P158R035 | 11-Jul-01 | 0 |
| 93 | P158R036 | 8-May-01 | 0 |
| 94 | P158R037 | 25-Jun-01 | 0 |
| 95 | P158R038 | 25-Jun-01 | 0 |
| 96 | P158R039 | 8-May-01 | 0 |
| 97 | P158R040 | 8-May-01 | 0 |
| 98 | P158R041 | 8-May-01 | 0 |
| 99 | P159R033 | 31-May-01 | 0 |
| 100 | P159R034 | 3-Aug-01 | 0 |
| 101 | P159R035 | 15-May-01 | 0 |
| 102 | P159R036 | 15-May-01 | 0 |
| 103 | P159R037 | 15-May-01 | 0 |
| 104 | P160R033 | 20-Jun-00 | 0 |

(Note the above list is being updated to 122 scenes)

Figure 2. Distribution of the proposed 122 scenes to be used for creating the EarthSat’s Customized GeoCover LC product for Afghanistan and surrounding area.

Landcover Categories

The landcover categories in the standard GeoCover LC product follow closely to those defined by Anderson et al. in his 1976 publication, “A land use and landcover classification system for use with remote sensor data”  (U.S.G.S. Professional Paper 964).  Brief descriptions of the 13-landcover categories used in the standard GeoCover LC product are shown below in Table 2.

Table 2. Brief Description of the Standard GeoCover LC Landcover Classes

| Class Number | Class Name | Class Description |
| --- | --- | --- |
| 1 | Forest, Deciduous | Woody vegetation > 3 meters (10 ft) in height that lose leaves periodically due to changing seasons or drought. Canopy closure must be >35% (<35% = Category 3). Also included in this category are areas commonly referenced as “swamp” or forested wetland if dominated by a deciduous canopy. |
| 2 | Forest, Evergreen | Woody vegetation > 3 meters (10 ft) in height that retain their leaves throughout seasons. Evergreen includes both needle leaf and broad leaf species. Some tree plantations may be included in this class. Canopy closure must be >35% (<35% = Category 3) |
| 3 | Scrub/Shrub | Woody vegetation less than 3 meters (10 ft) in height, with both closed and open canopies. Minimum ground cover is 10%; conversion to forest occurs at 35% canopy coverage provided the trees are > 3 m in height. Areas of forest that have experienced burning (burn scars) are classified in this category. |
| 4 | Grassland | Grass and herbaceous areas. Category may include herbaceous wetlands if images are collected during dry season or periods of drought. Land cover types commonly referenced as savanna, open savanna, and woody savanna are included in this category. Areas of grassland and scrub/shrub that have experienced burning (burn scars) are classified in this category. |
| 5 | Barren/Sparsely Vegetated | Includes sand dunes, desert, rock outcrops, bare soil other than bare agricultural land, and sparsely vegetated areas of grass and shrub. This category includes non-vegetated strip mines and quarries except where covered by development (urban/built-up) or water (water). |
| 6 | Urban/Built-Up | Cities, towns, wide roads, airports, other developed areas. Areas of non-urban cover within the urban fringe are only separated from the urban category if they exceed 25 ha (500 x 500 m if square or 307 pixels) in size and 2 pixels (58 meters) in width. |
| 7 | Agriculture, Other | All non-rice agricultural fields, both with crop or fallow; highly managed pastures and haylands (but not grasslands commonly referenced as “rangeland”); complex mosaics of natural vegetation and cropland. Some orchards and tree plantations, such as palm or date plantations, may be included in this category. |
| 8 | Agriculture, Rice | Paddy agricultural fields, mainly rice, that are seasonally inundated with water. Depending upon the season of acquired imagery, some rice paddies may be included in the “Agriculture, Other” class if the paddies are not flooded. |
| 9 | Wetland, Permanent Herbaceous | Emergent herbaceous wetlands, as well as other irregularly inundated areas that may not be vegetated, including: mud flats, saltpans, and playas. Vegetated herbaceous wetlands may be referenced as “marsh”. Areas commonly referenced as “swamp”, including forested wetlands, are not included in this wetland class. Forested wetlands, with the exception of “Mangrove” are included in one of the forest categories. Areas of burn scar within a wetland are included in this category. |
| 10 | Wetland, Mangrove | Regularly inundated coastal areas that are covered by mangrove species. Areas of burn scar within a mangrove wetland are included in this category. |
| 11 | Water | All type of water bodies, including rivers, lakes, reservoirs, ponds, bays, and estuaries. This categorization does not differentiate between these water classes. |
| 12 | Ice/Snow | Areas covered by permanent or nearly permanent ice and/or snow. |
| 13 | Cloud/Cloud Shadow/No Data | Areas in which the ground surface is masked by cloud, smoke, or thick haze, or their concurrent shadows. Also includes any area for which no meaningful Thematic Mapper signal is received, e.g., line drops, areas outside of the coverage of the outermost TM image footprint. |

This Customized GeoCover LC product will have 19 landcover classes as shown in table 3.

Table 3. Brief Description of the Proposed Customized GeoCover LC Landcover Classes

| Class Number/ GeoCover LC Class | Class Name | Class Description |
| --- | --- | --- |
| 1/1 | Forest, Deciduous | Woody vegetation > 3 meters (10 ft) in height that lose leaves periodically due to changing seasons or drought. Canopy closure must be >35% (<35% = Category 3). Also included in this category are areas commonly referenced as “swamp” or forested wetland if dominated by a deciduous canopy. |
| 2/2 | Forest, Evergreen | Woody vegetation > 3 meters (10 ft) in height that retain their leaves throughout seasons. Evergreen includes both needle leaf and broad leaf species. Some tree plantations may be included in this class. Canopy closure must be >35% (<35% = Category 3) |
| 3/3 | Scrub/Shrub | Woody vegetation less than 3 meters (10 ft) in height, with both closed and open canopies. Minimum ground cover is 10%; conversion to forest occurs at 35% canopy coverage provided the trees are > 3 m in height. Areas of forest that have experienced burning (burn scars) are classified in this category. |
| 4/4 | Grassland | Category may include herbaceous wetlands if images are collected during dry season or periods of drought. Land cover types commonly referenced as savanna and open savanna are included in this category. Areas of grassland and scrub that have experienced burning (burn scars) are classified in this category. |
|  | Barren | Includes rock outcrops, desert, bare soil other than bare agricultural land, sparsely vegetated areas of grass and shrub and bare soil sand dunes. This category also includes non-vegetated strip mines and quarries except where covered by development (urban/built-up) or water (water) |
| 5/5 | Barren - Bedrock | Barren or sparsely vegetated areas that primarily contain rock outcropping |
| 6/5 | Barren -Colluvial | Barren or sparsely vegetated areas that primarily contain eroded material found at the bottom or on the lower slopes of a hill. |
| 7/5 | Barren - Alluvial Fans | Barren portions of alluvial fans, the fan shaped accumulation of alluvial deposits usually found at gradient changes such where streams transition from mountains to valleys. These are sedimentary deposits formed by flowing water. |
| 8/5 | Barren -Alluvial Streams | Dry, non-vegetated, disturbed, river, stream, or gully deposits. These are also sedimentary deposits formed by flowing water. |
| 9/5 | Barren - Mines and Quarries | Barren areas where extractive industries (e.g. strip mines or quarries) are active, or have been active in the past. |
| 10/5 | Barren - Dunes | Barren or sparsely vegetated areas that are covered with, or subject to dunes. |
| 11/6 | High Intensity Developed | Cities, towns, wide roads, large buildings and/or industrial complexes and other intensively developed areas, often considered the urban core. Areas of non-urban cover within the urban fringe are only separated from the urban category if they exceed 25 ha (500 x 500 m if square or 307 pixels) in size and 2 pixels (58 meters) in width. |
| 12/6 | Low Intensity Developed | Less intensively developed potions of cities and towns, and villages large enough to identified in the ETM data. This includes lower density residential, and light commercial and industrial areas. As with the high intensity developed class, areas of non-urban cover within the urban fringe are only separated from the urban category if they exceed 25 ha (500 x 500 m if square or 307 pixels) in size and 2 pixels (58 meters) in width. |
| 13/7 | Agriculture – Irrigated | All non-rice agricultural fields, that are irrigated, are near a water source/and or have irrigation infrastructure. Some orchards and tree plantations, such as palm or date plantations, may be included in this category |
| 14/7 | Agriculture – Rain Fed | Non irrigated agriculture areas. These areas include both active and inactive (due to moisture limitations, recently abandoned cropland) agricultural areas. This class also includes highly managed pastures and/or haylands (but not less managed grasslands commonly referenced as “rangeland”); as well as complex mosaics of natural vegetation and cropland. . |
| 15/8 | Agriculture - Rice | Paddy agricultural fields, mainly rice, that are seasonally inundated with water. Depending upon the season of acquired imagery, some rice paddies may be included in the “Agriculture, Irrigated” class if the paddies are not flooded. |
| 16/9 | Wetlands | Regularly or irregularly inundated areas that may be vegetated (emergent herbaceous wetlands) as well as others that may not be vegetated, including: mud flats, saltpans, and playas. This category includes vegetated herbaceous wetlands that are often referred to as “marsh”. Areas commonly referenced as “swamp”, including forested wetlands, are generally not included in this wetland class. Forested wetlands are included in one of the forest categories. Areas of burn scar within a wetland are included in this category |
| 17/11 | Water | All type of water bodies, including rivers, lakes, reservoirs, ponds, bays, and estuaries. This categorization does not differentiate between these water classes |
| 18/12 | Snow/Ice | Areas covered by ice and/or snow (generally permanent or nearly permanent) at the time of image acquisition. |
| 19/13 | Clouds/Shadows | Areas in which the ground surface is masked by cloud, smoke, or thick haze, or their concurrent shadows. Terrain shadows that completely mask the land cover are also included in this class. |

EarthSat’s Customized GeoCover LC Products

EarthSat proposes to deliver three rasterized landcover products as described below:

1) Landcover Raster File with No Minimum Mapping Unit for Full TM Scene in UTM Projection in ERDAS IMAGINE 8.4 Format

This land cover file has not been filtered or processed to a user-specified minimum mapping unit (MMU).  Consequently, it will have inherent speckle and noise of raster data categorizations from remotely sensed data.  The speckle and noise is removed when this data set is clumped to the user-specified minimum mapping unit. This UNCLUMPED raster file will be an 8-bit ERDAS IMAGINE file with cell values that indicate the landcover codes (see Table 3 for these codes).  Fig. 3 and 4 provide examples of EarthSat’s standard GeoCover LC  product .

2) Land Cover Raster File with a Minimum Mapping Unit for Full TM Scene in UTM Projection in ERDAS IMAGINE 8.4 Format

This landcover file will be processed to remove much of the speckle and noise associated with landcover categorizations based upon Landsat TM data.  The only difference between this file and the previous file is the incorporation of EarthSat’s CLUMP and ELIMINATE routines to generalize the land cover to a user specified minimum mapping unit.  EarthSat’s CLUMP routine is used to define the size of all contiguous features with the same landcover code.  EarthSat’s ELIMINATE routine removes any contiguous features of the same landcover code (with the exception of water) that were smaller in size than the user-specified minimum mapping unit.  The predominant land cover surrounding the eliminated clump replaces the areas of small clumps that are eliminated.  Note that the procedure employed using CLUMP and ELIMINATE will not remove narrow linear features with areas exceeding the user-specified minimum mapping unit that would be removed if standard filtering procedures were used to create the minimum mapping unit.  Landsat TM data typically can be used to generate maps at scales as large as 1:100,000.  At this scales, EarthSat would recommend a minimum mapping unit between 1 and  4 ha.  For water, a 0.2-hectare MMU (approximately 30m by 30m) will be used. This landcover raster with a minimum mapping unit will be an 8-bit ERDAS IMAGINE file with the landcover codes as shown in Table 3.  An example of this product is shown in Figure 5.  The size of the MMU can be specified by the client.

3) Land Cover Raster File with a Minimum Mapping Unit Tiled to Correspond with the 150 km by 150 km Cells used in the Orthorectified ETM imagery in UTM Projection in ERDAS IMAGINE 8.4 Format

This file contains all landcover classes and is a raster file in ERDAS IMAGINE 8.4 format.  This is an eight-bit/pixel file. The file is in UTM projection (Zone 42 WGS 84) clipped precisely to 150 km by 150 km cells.  There will be 120 of these cells to cover the entire study area.

Optional Vector Coverages

If desired, EarthSat can reproject the rasterize landcover product to Geographic projection and clip the geographic raster product to 1-degree by 1-degree tiles.  There will be approximately 224 1-degree by 1-degree tiles to cover this study area.  The clipped and reprojected raster files will be vectorized using EarthSat’s proprietary algorithm (RTOV) that reduces the number of vertices within a line segment.  EarthSat’s vector file is then imported as an ARC/INFO coverage. Only one vector file of all landcover classes will be delivered.

The vector coverages are checked to insure that there are no label errors and that the coverages are fully topologically consistent.  The coverage will contain all 19 landcover classes. Each polygon in this coverage will be attributed with two variables, LANDCOVER and GRID_CODE.  The LANDCOVER values will be the landcover class names as shown in Table 3.  The GRID-CODE values will be 0 – 19 representing each of the landcover classes.  This ARC coverage is exported using the command shown below:

EXPORT <coverage>  <exchange file> NONE.

Using NONE as the compress option in ARC/INFO has resolved a problems in importing these files with ArcView.  These files are compressed with UNIX COMPRESS and can be uncompressed with UNIX UNCOMPRESS or Windows WINZIP.

### Ground Truth

The accuracy of EarthSat’s Customized GeoCover LC improves as the availability of ground truth increases.  During the last 30 years EarthSat has processed over 30,000 Landsat TM scenes world-wide for a variety of user applications.  This wealth of international experience has given EarthSat the opportunity and challenge to search, locate, and acquire a vast array of ground truth data including thousands of site visits worldwide.  In conjunction with this project, EarthSat will continue to expand ground truth collection using all sources possible.  EarthSat has also developed techniques to propagate small samples of ground truth throughout a region in a similar manner as GeoCover Ortho utilizes a small set of very accurate geodetic control to provide geometric control to a large number of images.  EarthSat also has a great deal of experience processing remotely sensed images for land cover interpretation for the US government where NTM and other NIMA data provided much of the ground truth information.  EarthSat understands the great value NTMs can provide as another component in ground truth compilation and would like to work with the client to take advantage of this information.  For this project,  EarthSat is requesting up to 150 frames of NTMs.  Based upon our experience, we believe this additional ground truth information will greatly enhance the accuracy of the landcover categorization.  EarthSat maintains a SCIF and has a staff of cleared personnel who are accustomed to using this information as an input into TM landcover categorizations.  Any NTMs provided for this project would be used only on for this project and will be returned to the client immediately upon completion of this project.

Data Rights

EarthSat is providing EarthSat’s standard GeoCover LC to NIMA as a commercial product with exclusive commercial rights retained by EarthSat and NIMA retaining a full Government Purpose license.  Under this arrangement, NIMA is granted an unlimited license to use, distribute, disseminate, modify, and update EarthSat’s GeoCover LC Version 1.0 products. EarthSat owns the GeoCover LC Version 1.0 products and has similar rights as NIMA to use, distribute, disseminate, modify, and update EarthSat’s GeoCover product.  In addition to the unlimited Government Purpose Rights to use, distribute, disseminate, and update GeoCover LC, the Government retains the right to insert GeoCover into other products that the Government decides may or may not become publicly available, as long as the EarthSat copyright of the GeoCover LC is displayed on the publicly available product.

For this project, the client will own EarthSat’s Customized GeoCover LC product and the client has absolute, unrestricted rights to this product.  EarthSat reserves the right to recode the 19-class landcover product to the 13-class landcover product as shown in Table 3 and to retain this product as input to EarthSat’s Standard GeoCover LC product.  EarthSat will have no rights the 19-class landcover product.  EarthSat will propose to NIMA to reformat this product to meet NIMA’s specification for the Standard GeoCover LC product for only the cost of reformatting and distribution.

### Delivery Schedule

EarthSat anticipates requiring over 80 staff hours per Landsat ETM scene processed.  EarthSat can create a team of 10 image analysts without impacting EarthSat’s current US contracts.  Using a team of 10 analysts, the product can be produced in 4.5 months from the completion of the orthorectification of the Landsat ETM images.  EarthSat can create a team of 20 image analysts and create this product in 2.5 months from the completion of the orthorectification of the Landsat ETM images.  However, to create a team of 20 image analysts, EarthSat will need to modify the delivery schedule of the standard GeoCover LC products to NIMA.  By using EarthSat’s entire GeoCover LC team and additional EarthSat employees, the 19-class landcover raster products can be produced in approximately 1 month.

Cost

EarthSat’s anticipates a cost of approximately $5,500 per scene for a total cost of  $671,000 to create the raster landcover products described above for the entire 122-scene study area.  The cost per scene applies if 50 or more scenes are tasked.

# Text boxes

# Afghanistan 122 Scene Mosaic

Magenta Box 150 km UTM mosaic blocks (128 tiles)

Green 122 Landsat TM scenes

Forest - Deciduous DDeciduous

Forest - Coniferous

Scrub / Shrub

Grasslands

Barren/Sparsely Vegetated

Urban / Built up

Agriculture - Rice Fields

Agriculture - Other

Wetlands

Wetlands - Mangroves

Water

##### Ice/Snow

No Data / Clouds / Shadows

Figure 3. Example of  EarthSat’s Standard GeoCover LC Product

Figure 4. Example of EarthSat’s GeoCover LC product before application of minimum mapping unit.

Figure 5.  Example of GeoCover LC product after application of minimum mapping unit.