CONSTRUCTION JOB HAZARDS ANALYSIS

SCAFFOLDING

Contractor Name: __________________________	   Date: _____________

| Scope of Work | Potential Safety Risks/Issues | Mitigation of Potential Risks |
| --- | --- | --- |
| General, Site and work area setup |  | All work shall be in accordance with the subcontractor’s IIPP and in conformance with all LBNL policies, Federal OSHA & Cal-OSHA standards; All general safety orders shall be reviewed by subcontractors prior to starting work; All equipment shall be properly and completely inspected by its operator prior to use. Any equipment that is not fully operational and function shall be removed from service; All extension cords are to be in good working order, free from cuts and abrasions and properly grounded and of a gauge suitable for the amperage used; All power equipment shall be in good working order and only operated by trained employees; In areas where the PEL’s cannot be measured to ensure employees are not being exposed to OSHA permissive exposure limits, employees will wear OSHA and NOISH approved breathing apparatuses including particulate masks. If such apparatuses are use, employees shall be FIT tested and their certification cards shall be made available to an LBNL representative upon request; Power tools found not to be in good working order and unsafe to use shall be tagged and removed from the work area; employees using tools are to be trained in their safe use and the safety rules for them and PPE required at all times including; Hard Hats Safety Glasses Respirators as necessary Masks Proper Gloves as necessary Noise Protection |
| General Requirements |  | Specific requirements pertaining to the erection of scaffolding will be found in 29 CFR 1926.451. A competent person is defined as, one who is knowledgeable through training or experience as set forth in the requirements of 29 CFR 1926.451. Prior to use on each shift, a competent person as assigned by the Site Contractor will perform inspections of all scaffolds used and document the inspection on the scaffold tag. The footing of scaffolds must be sound and rigid, capable of supporting the weight of the scaffold and its intended load Only qualified persons shall erect, dismantle, move or alter scaffolds. All scaffolds shall have top rails, intermediate rails and toe boards installed on all open sides Guardrails shall have a toprail between 38 inches and 45 inches high above the platform surface and have supports not to exceed 8 feet between vertical posts. Toe boards shall be 4 in. high Scaffolds and components shall be able to support at least four times the intended load Any components of a scaffold damaged or weakened shall be repaired or replaced immediately. All planking for platforms shall be overlapped at least 12 inches and secured from movement Straight and/or extension ladders shall be provided for safe access to all scaffolds and work platforms. The use of a scaffold system with built-in ladder is permitted. The top of each ladder shall be secured with wire or rope. Also, the ladder shall extend at least 36 inches above the work platform. Climbing on cross braces is not permitted Scaffold planks shall extend over their end supports at least 6 in, but not more than 12 inches and shall be wired down or otherwise secured from movement Legs and uprights of scaffold shall be plumb and rigidly braced to prevent swaying Overhead protection shall be provided for personnel on a scaffold exposed to overhead hazards. Overhead protection shall also be provided for employees passing by or under scaffolds that pose overhead hazards Wire or wire rope used for scaffold suspensions shall be capable of supporting six times the intended load. Although it is required that each scaffold be inspected by a competent person, it is the responsibility of each user to check his/her scaffold prior to each use to ensure it is safe and properly tagged A competent person shall place a white inspection tag on every scaffold for daily inspection. A green tag indicates that the scaffold is complete and safe to use with no additional precautions A yellow tag indicates that the scaffold requires additional fall protection equipment as indicated on the back of the tag. A red tag indicates an unsafe scaffold and is not to be used. The only person who may enter a redtagged scaffold is a trained scaffold builder while completing or doing repairs on the scaffold. If a scaffold has no tag, it is not to be used until inspected and properly tagged. If a scaffold is found to be deficient or unsafe and is tagged green or yellow, the tag should be immediately removed and the Site Contractor notified. |
| Climbing | Striking against other objects Fall to a different level Slip/trip Overexertion, strain, sprain | Be aware of surroundings Wear full body harness when working 6’ above deck with lanyard or Arrestive Fall Device (A.F.D.) Maintain Proper footing Maintain proper body positioning at all times |
| Descending | Striking against other objects Being struck by other objects Caught in between objects Fall to a different level Fall on the same level Slip/Trip Overexertion, strain, sprain | Be aware of surroundings Wear full body harness when working 6’ above deck and secured lanyard Maintain proper footing Maintain proper body positioning at all times Use Hand Rails |

General mitigating requirements are as follows:

- All employees shall be aware of General Safety Rules.

- All employees shall be aware and trained in the Illness & Prevention Program.

- All employees shall be aware and trained in the Chemical Hazards Communication Program.

- All MSDS for proposed and used chemicals shall be on file and approved with the General Contractor prior to the start of work. Provide training as required by the specific MSDS.

- All PPE shall be used in accordance with the applicable MSDS.

- All employees, where required shall be trained and certified when required by OSHA & Cal-OSHA.

- All PPE to be approved by ANSI or applicable approval agency.

- All MSDS sheets shall be submitted to the General Contractor prior to starting work.

- Fall protection measures shall be in place for ladder safety in heights of 6 feet and higher.

- Any injury is to be reported to the Supervisor immediately

______________________________________________________	_____________________

Agreed To –                        							Date

______________________________________________________	_____________________

Approved –                                							Date

______________________________________________________	_____________________

Reviewed / Approved – Lawrence Berkeley National Lab			Date

A signed copy of this JHA must be posted while the applicable subcontractor is working on-site and be available to any LBNL employee upon request.

Copy Distribution:

General Contractor	        Project Superintendent    	   	   Subcontractor

LBNL Safety Officer            LBNL Construction Manager

Construction JHA Safety Sign-in Sheet

Date: __________

Print                                                                      Signature

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________

___________________________________        ___________________________________