FROM PRESENT SURVEYING TO FUTURE PROSPECTING OF THE ASTEROID BELT.  P.E. Clark1 S.A. Curtis2, M. Rilee1, and C. Cheung2, 1Affiliation: L3 Communications, Government Services, Inc., 3750 Centerview Drive, Chantilly, VA 20151, Correspondence: Code 695, NASA/GSFC, Greenbelt, MD 20771, Email: Pamela.clark@ gsfc.nasa.gov, 2Affiliation: Code 695, NASA/GSFC, Greenbelt, MD 20771.

Introduction: We have applied a future mission architecture, the Autonomous Nano-Technology Swarm (ANTS), to a proposed mission for in situ survey, or prospecting, of the asteroid belt, the Prospecting Asteroid Mission (PAM) as part of a NASA 2003 Revolutionary Aerospace Concept (RASC) study.[1] ANTS architecture builds on and advances recent trends in robotics, artificial intelligence, and materials processing to minimize costs and maximize effectiveness of space operations [2,3,4,5,6,7,8]. PAM and other applications [1,9,10,11,12] have been proposed for the survey of inaccessible, high surface area populations of great interest from the standpoint of resources and/or solar system origin.

The ANTS architecture is inspired by the success of social insect colonies, a success based on the division of labor within the colonies in two key ways: 1) within their specialties, individual specialists generally outperform generalists, and 2) with sufficiently efficient social interaction and coordination, the group of specialists generally outperforms the group of generalists. Thus systems designed as ANTS are built from potentially very large numbers of highly autonomous, yet socially interactive, elements. The architecture is self-similar in that elements and sub-elements of the system may also be recursively structured as ANTS on scales ranging from microscopic to  interplanetary distances.

Here, we analyze requirements for the mission application at the low gravity target end of the spectrum, the Prospecting Asteroid Mission (PAM), and for specialized autonomous operations which would support this mission [1,10,11,12]. ANTS as applied to PAM involves the activities of hundreds of individual specialist ‘sciencecraft’. Most of them, called Workers, carry and operate eight to nine different scientific instruments, as listed in the table, including spectrometers, ranging and radio science devices, and imagers. The remaining specialists, Messenger/Rulers, provide communication and coordination functions among specialists operating autonomously as individuals, team members, and subswarms. Individual nanocraft are on the order of a kilogram in mass, translating into gossamer structures. Onboard power requirements, met by small nuclear batteries, must be on the order of milliwatts. The non-expendable propulsion system is based on autonomously deployable and configurable solar sails, a system suitable to low gravity well targets.

Methodology:  The first step in this process was the development of a patented conceptual model, called a neural basis function, which combines the capability of autonomous and collective interaction, or bi-level intelligence, for each component, subsystem, or agent [1].  Individual operational components connect to other operational components and to heuristic level decision making components through a specially designed interface.  This structure is redundant at each level. We have also generated scaled physical models of spacecraft both packaged and fully deployed, as well as of onboard structures such as solar sail and instrument platform. to illustrate the modularity, configurability, and orders of magnitude scalability. Formulation of requirements and operational scenarios for PAM [1], including propulsion, navigation, and data taking operational interactive requirements and scenarios, are driven by the variable size and irregular mass distribution and meteoritic composition of asteroid targets in the surrounding low gravity environment.

Discussion:  The Figure illustrates the application of the neural basis function in the context of a survey mission.  Potential science goals for PAM provide this context (Table). Mainbelt asteroids highly variable in composition and/or dynamic properties. Potential targets are separated by distances of hundreds of thousands of kilometers making detection and location a problem. The numbers and distances require large numbers of multi-specialist teams.

What would the structure and size of a swarm of specialists need to be?  If a minimum of four specialists are needed for collective decision making, as required in the neural basis function (Figure), and we allow for ten instrument specialist teams (Table), that means a minimum size of 40 in a subswarm.  Allowing for five to ten percent attrition over the few years required for a survey, numbers of specialists should  be a minimum of 50 in a subswarm. The use of ten to twenty of such subswarms should allow for the in situ characterization of hundreds of asteroids over the course of the traverse of the belt. The difficulty in observing irregular, rapidly moving, and often poorly illuminated objects is largely overcome by the ANT sciencecraft capability to optimize of viewing conditions for each instrument, a capability which drives the need for revolutionary ANTS architecture. Each specialty would have different viewing requirements and thus operational scenarios. Increasing the numbers in each specialty team could speed up the process of data collection for spectrometers, which have the most stringent requirements, and potentially allow for higher resolution mapping.  For this reason, we prefer to double subswarm size to approximately 100.

Our concept includes autonomous assembly and packaging of components prior to deployment. Configurable, addressable modular components form smart, self-deploying systems for assembly operations driven by the need for minimize bandwidth (resources) and human involvement (labor). Components would be composed of carbon nanotubule strands (tethers) or fibers (surfaces) reversibly spooled and deployable from NEMS nodes, allowing for orders of magnitude decrease in packaging volume. 1000 smart 10 centimeter, 1 kg cubic boxes would create a 1000 kg 1 meter cube.  Distributed networks of messengers, with enhanced communication systems, would store, transmit, and carry data over interplanetary distances.

Conclusions: The ANTS approach would allow simultaneous survey of many interesting asteroids by teams of flexible instrument specialists configured for optimal operation.  Redundancy allows for planned high attrition of individual workers, including the return of communication specialists, or messengers, without compromising ongoing prospecting.  Use of scalable, reversibly deployable gossamer structures would minimize the weight and power requirements, allowing maximum change in configuration during operation as well as minimum packaging size prior  to deployment.  These studies imply that ANTS architecture is an efficient approach for studying the asteroid belt, depending only on already anticipated incremental advances in technology.

References: [1] Curtis et al (2004) The Autonomous NanoTechnology Swarm, NASA RASC Final Report (in preparation); [2]Curtis et al (2000) Abstracts of IAF, 51st Congress; [3] Clark et al (2001) AAS/DPS, BAAS, vol. 33, no. 3; [4] Clark et al (2001) EOS Trans. AGU, 82 (47), 2001; [5] Clark et al (2002) LPSC XXXIII, 1394; [6] Clark et al (2002) EOS Trans AGU, P521-01, [7] Curtis et al (2003)Abstracts, 3rd Intl Workshop on Satellite Constellations and Formation Flying, Pisa, Italy; [8] Clark et al (2003) 34th LPSC; [9] Curtis et al (2003) Saturn Autonomous Ring Array, NASA RASC Proposal; [10] Rilee et al [2002] IEEE Aerospace Conf, Big Sky, MT, 209; [11] Curtis et al (2003) IEEE Aerospace Conference, Big Sky, MT; [12] Curtis et al (2003), Large Autonomously Reconfigurable Antennas for Space-based Radio Astronomy, NASA MSMT Proposal.

Acknowledgment: Support for this work has been provided through NASA contract NAS5-99189, subcontract 0299189EER, with ITMI.

Return to or visit ANTS home or SARA web page:

http://ants.gsfc.nasa.gov/pamtest/website.html

http://ants.gsfc.nasa.gov/pamtest/pam.html

| Science Context Table for PAM |
| --- |
| Modes of Study | Interior structure and origin | Surface characterization with spectrometers | physical/Dynamic | Detection/Location |
| Measurements | magnetic field | compositional variations | photogeology,stratigraphy | regolith particle properties | mineral assemblages | volatiles, organics | major, refractory elements | morphology,gravity,spin | imaging triangulation |
| Specialists | Magnetometer | All spectrometers | Visible Imager | Thermal/Radio Sounder | UV/Vis/IR | Neutron/Gamma-ray | X-ray/Gamma-ray | Imagers/Rangers/Radio Science | Visible Imagers |

# Text boxes

Three Dimensional Multi-level System Interactions at every scale

Housekeeping

Instrument

Communication

Ruler/Control Subsystem

Navigation & Propulsion

Worker Team

Worker

Worker

Worker

Ruler/

Communicator

Worker