PERFORMANCE WORK STATEMENT

FAA LOGISTICS SUPPORT FACILITY

TEST EQUIPMENT REPAIR AND CALIBRATION SERVICES

MARCH 2006

TABLE OF CONTENTS

C-1.  GENERAL	1

1.1  SCOPE OF WORK	1

1.2  BACKGROUND INFORMATION	1

1.3  CONTRACTOR RESPONSIBILITIES	1

1.4  WORKLOAD PROJECTIONS	1

1.5  PERSONNEL	2

1.5.1  Key Personnel	2

1.5.1.1  Contract Manager	2

1.5.1.2  Metrologist	3

1.5.2  Technicians	3

1.5.3  Qualifications Review	3

1.5.4  Personnel Training	3

1.5.5  Personnel Reporting Requirements	4

1.5.5  Personnel Reporting Requirements	4

1.6 ADMINISTRATIVE	4

1.6.1  Security	4

1.6.1.1  Contractor's Security Point of Contact	4

1.6.1.2  Data Systems Security	4

1.6.1.3  Physical Security	4

1.6.1.3.1  Contractor Controlled Access	5

1.6.1.3.2  Contractor Package Inspection	5

1.6.1.3.3  Stolen, Missing, or Damaged Government Property	5

1.6.1.3.4  Stolen, Missing, or Damaged Personal Property	5

1.6.1.4  Security Inspections	6

1.6.1.5  Compliance with Security Directives	6

1.6.1.6  Key Control	6

1.6.2  Vehicle Registration	6

1.6.3  Smoking Policy	7

1.7  QUALITY	7

1.7.1  QUALITY CONTROL	7

1.7.2  QUALITY ASSURANCE	8

1.8  PERFORMANCE EVALUATION MEETINGS	8

1.9  HOURS OF OPERATION	8

1.9.1  On-Call Emergency Support	9

1.9.2  Federal Holidays	9

1.10  CONTINGENCIES	10

1.10.1  Contingency Plan	10

1.10.2  Strike Contingency Plan	10

1.11  ENVIRONMENTAL PROGRAMS	10

1.11.1  Regulations/Laws.	10

1.11.2  Compliance Requirements	11

1.11.3  Citations	11

1.12  ENERGY AND UTILITIES CONSERVATION PROGRAMS	11

1.12.1  Conservation Instruction	11

1.13  ACCESS LIMITATIONS	11

1.13.1  Restricted Areas	11

1.13.2  "Off Limits" Areas of Facilities	12

1.13.3  Interference with Contractor Performance	12

1.14  INSPECTION BY REGULATORY AGENCIES	12

1.15  SAFETY REQUIREMENTS AND REPORTS	12

1.15.1  Accident Reporting	13

1.16  TRANSITION REQUIREMENTS	14

1.16.1  Transition Period	14

1.16.2  Phase-Out	14

1.17  PWS Reference Information	15

C-2  DEFINITIONS	15

C-3   GOVERNMENT-FURNISHED PROPERTY AND SERVICES	20

3.1  EQUIPMENT AND INSTALLED PROPERTY	20

3.2  FACILITIES	20

3.3  GOVERNMENT-FURNISHED MATERIAL (SHOP STOCK)	21

3.4  DOCUMENTS AND FORMS	21

3.5  ACCOUNTABILITY FOR GOVERNMENT-FURNISHED PROPERTY	21

3.5.1  Property Control Procedures	22

3.5.2  Initial Government-Furnished Property Inventory	22

3.5.3  Government Furnished Equipment Warranties	22

3.5.4  Annual Inventory	22

3.5.5  Phase-Out Inventory of GFE	23

3.5.6  Disposition of Property	23

3.5.7  Obtaining Additional GFE Property	24

3.5.8  Equipment Repair	24

3.5.9  Replacement of Equipment	24

3.5.10  Applicable Manufacturer's Literature	24

3.5.11  Damage Reports	25

3.6  SERVICES.	25

3.6.1  Utilities	25

3.6.2  Custodial	25

3.6.3  Copier Equipment and Supplies	25

3.6.4  Postal	25

3.6.5  Telephone Services	26

3.6.6  Real Property Maintenance	26

3.6.7  Center Civil Engineering	26

3.6.8  Security Services	26

C-4  CONTRACTOR FURNISHED PROPERTY	26

4.1  PROPERTY	26

4.2  ADMINISTRATIVE SUPPLIES	27

4.3  TOOLS	27

4.4  TEST EQUIPMENT	27

4.5  FUELS	27

4.6  MATERIAL AND PIECE PARTS	27

4.7  PERMITS	28

4.8  CUSTODIAL SERVICES	28

C-5  SPECIFIC TASKS	28

5.1  GENERAL	28

5.1.1  Work Management	28

5.1.2  Budget Preparation	29

5.1.3  Records and Filing Systems.	29

5.1.3.1  Records	29

5.1.3.2  Filing System-Work Orders	29

5.1.4  Reports	29

5.2  TEST EQUIPMENT REPAIR AND CALIBRATION SERVICES	30

5.2.1  In-processing Equipment	30

5.2.2  Workload Programs	30

5.2.3  Workload Priorities and Turn Around Times (TAT)	32

5.2.3.1  Delinquent Priorities	33

5.2.3.2  Credit	33

5.2.3.3  Program Warranties	34

5.2.4  Workload Item Completion	35

5.2.5  Calibration and Repair Criteria	35

5.2.5.1  Calibration and Certification	35

5.2.5.1.1  Primary Standards	35

5.2.5.1.2  Working Standards	35

5.2.5.1.3  Calibration Certificates	35

5.2.5.1.4  Environmental Control	35

5.2.5.2  Repair	36

5.2.5.2.1  Replacement Parts/Components	36

5.2.5.2.2  Certification Labels and Stickers	36

5.2.5.2.3  Beyond Economical Repair/Survey and RTO	36

5.2.5.2.4  Cannibalization	37

5.2.5.3  Modifications	37

5.2.5.4  Calibration Recall System	37

5.2.5.5  Cleaning	38

5.2.6  Other Tasks	38

5.2.6.1  Technical References	38

5.2.6.2  Contractor Developed Procedures	38

5.2.6.3  Workload Item Receiving	38

5.2.6.4  Ancillary Equipment	38

5.2.6.5  Manufacturers Warranties	38

5.2.6.6  Subcontracting	39

5.2.6.7  Workload Item Control	39

5.2.6.8  Documentation	39

5.2.6.9  Disposition Of Failed Equipment Due Calibration	40

5.2.6.10  Condition Tags	40

C-6  APPLICABLE DOCUMENTS	40

6.1  General	40

6.2  Mandatory Directives	41

6.2.1  Directive Revisions	41

6.3  Required Forms	41

LIST OF ATTACHMENTS

TECHNICAL EXHIBITS (TE)

TE-1A…………………………….……..Classification for Bid, FY-05 Calibrations

TE-1B……………………………..…………..Classification for Bid, FY-05 Repairs

TE-2A………………………….…Estimated Workload for FY-07 through FY-11

TE-2B………………………………………………………FY-05 Workload by Priority

TE-3……………………………………….………………………….FY-05 Parts Utilized

TE-4……………………………………………….………………..FY-05 Obsolete Parts

TE-5…………………………..……………...….FY-05 Equipment Sub-Contracted

TE-6……………………….……….…..Government Furnished Equipment (GFE)

TE-7…………………………………………………………...Manuals and Procedures

TE-8……………………….…………..……Test Equipment Lab Floor Plan/Space

TE-9……………………………………………………..….FAA Applicable Documents

TE-10……………………………………………………….…..Required Reports/Plans

TE-11………………………………..……….Examples of Forms and Labels Used

# C-1.  GENERAL

## 1.1 SCOPE OF WORK

The Contractor shall provide all services, personnel, material, supplies, supervision, labor, and equipment, except that specified as Government-furnished, required to operate the Test Equipment Repair and Calibration work center of the FAA Logistics Center (FAALC) at the Mike Monroney Aeronautical Center (MMAC) by performing the services described in this Performance Work Statement (PWS). The Contractor shall provide related services as specified, in accordance with all terms, conditions, general and special contract requirements, specifications, drawings, attachments and exhibits contained herein or incorporated by reference.

## 1.2 BACKGROUND INFORMATION

The FAALC is located within the MMAC, Oklahoma City, Oklahoma.  The MMAC is a service and support facility for the Federal Aviation Administration (FAA).  The major responsibility of the FAALC is supply support of the National Airspace System (NAS).  Electronic test equipment and other measurement systems serviced by this facility are in the direct support of the NAS.  The Test Equipment Repair and Calibration function operates and maintains laboratory standards. Its primary duties are calibrating, repairing, cleaning, modifying, reconditioning, and certifying test equipment and ancillary measurement systems to original manufacturers specifications.

## 1.3 CONTRACTOR RESPONSIBILITIES

The Contractor's work and responsibilities include all Contractor planning, programming, administration, financial control, supply, quality assurance and management necessary to provide the service specified herein. The work shall be conducted in accordance with this contract and all applicable Federal, State and local laws, regulations, codes, or directives, to include documents listed in Technical Exhibit-9. Contractor employees shall observe and comply with all fire, safety, environmental, security, traffic, parking, and observe all “off-limits” areas. Possession of firearms or other lethal weapons are not allowed on the MMAC.

## 1.4 WORKLOAD PROJECTIONS

TE-2A Estimated Workload provides historical FY-05 work counts by specific programs and provides future estimates. TE-2B provides historical FY-05 workload by priority. The workload projections represent the Government's best estimate for each specific task required in this PWS for FY-07 through FY-11.

## PERSONNEL

The contractor shall provide a sufficient number of qualified personnel to perform the work described in this PWS in accordance with the timeliness requirements specified in section 5.  These personnel shall provide the core of knowledge for the Contractor to ensure uninterrupted performance at acceptable quality levels.  Personnel assigned to this contract must be fully capable of reading, writing, understanding, and speaking common English.  All personnel shall be United States citizens or resident aliens.

The contractor shall designate sufficient supervisory personnel to meet task outcomes.  Contract supervisors will provide day-to-day supervision of contract personnel including, but not limited to, work monitoring, payroll records, leave, etc.  At no time will contractor personnel be supervised by FAA personnel.  Government assistance will be available to provide technical and policy guidance through the assigned COTR.

The following minimum requirements shall be met for contractor personnel assigned under this PWS:

### 1.5.1 Key Personnel

The following key personnel shall provide management, administrative and technical interface with FAA personnel in the day-to-day accomplishment of these PWS requirements.  The names of these individuals and their alternates shall be designated in writing in the Contractor's Quality Control Plan and other plans as required.  Any proposed changes to these individuals must be approved in writing by the C.O.

#### 1.5.1.1 Contract Manager

The contractor must assign a manager who shall have final responsibility for the contract.  This individual shall have full authority to act for the contractor in all day-to-day matters relating to contractor performance and shall work with the Government's Contracting Officer Technical Representative (COTR) in the administration, management, performance, and procedural and technical matters pertaining to this contract.  The Contract Manager shall be physically present on site at the FAALC, except on legal federal holidays, during the core hours of 8:00 AM to 4:30 PM, Monday through Friday. An alternate shall be designated in the Contract Manager’s absence. The Contractor shall provide telephone numbers of the Manager and alternate(s) where these persons may be contacted outside of normal duty hours.  The Contract Manager and any individual(s) designated to act for the Contractor shall have full authority to contractually commit the Contractor, and act without delay on matters pertaining to execution of the contract.

#### 1.5.1.2 Metrologist

The metrologist shall have considerable knowledge of metrological labaoratory methods and procedures with a minimum of seven years calibration laboratory experience. The metrologist shall have experience maintaining calibration reference standards for basic electrical measurements, transferring the integrity of reference standards to working standards, and developing new methodologies for state-of-the-art electrical measurements.  Knowledge of maintaining and calibrating barometric pressure standards is required.  The metrologist shall be capable of developing manual/automated calibration procedures as required.

### 1.5.2 Technicians

The technicians shall have experience in performing functions such as operation, troubleshooting, maintenance, repair and calibration of voltage, current, power, impedance, frequency, microwave or barometric pressure measurement.  A knowledge of electrical theory, electronics and physics and operating principles of precision measurement equipment (PME), including calibration and working standards, interpretation of schematic wiring diagrams, blue prints, technical publications, use and care of calibration standards, PME and metrology is desired.

### 1.5.3 Qualifications Review

The contractor shall present all pertinent qualification credentials to the CO for subsequent review, approval or disapproval.  The CO shall have final approval authority as to acceptance or non-acceptance of all contractor nominated management and technical personnel for the positions in this contract.  The CO may waive the mandatory experience requirements upon presentation of evidence of equivalent experience in a related field.

### 1.5.4 Personnel Training

The Contractor shall provide for all training required to meet requirements of the PWS, unless otherwise specified herein or as otherwise approved by the CO.  Training records shall be maintained for each employee.

### 1.5.5 Personnel Reporting Requirements

The contractor shall provide to the C.O, the names, shift, job title, and other pertinent information requested of all employees with Government ID badges who are in the contractor's employ as requested.

## 1.6 ADMINISTRATIVE

### Security

#### 1.6.1.1 Contractor's Security Point of Contact

The Contractor shall designate an on-site point of contact through which the Government may direct security-related questions.  This employee shall be designated in writing to the CO prior to the start of the base year performance period.

#### 1.6.1.2 Data Systems Security

Data security must be provided via terminal restrictions as prescribed by the Aeronautical Center Office of Information Services standard operating procedures.  These procedures are in accordance with standards prescribed by the Comptroller General, the Department of Transportation, the Office of Management and Budget, and the Department of Defense, including the Federal Information Processing Standards (FIPS) publications.  The Contractor shall comply with FAA Order 1370.82, Information Systems Security Program and the Federal Information Security Management Act (FISMA). The FAA will provide all support contractors annual security awareness briefings.  The Contractor shall be responsible for monitoring and controlling access to all automated system databases.  The contractor shall register all personnel authorized to use the computer systems by completing required request for Computer Data Access forms as directed by the CO.  Only those Contractor personnel so authorized shall operate these data systems.  Any passwords assigned shall only be used by authorized contractor personnel.  Upon termination of employment, the contractor shall delete affected individual's assigned password(s) from the system.

#### 1.6.1.3 Physical Security

Contractor personnel working within Government facilities are responsible for compliance with applicable building and physical security requirements in accordance with FAA Order 1600.69, FAA Facility Security Management Program.  These requirements include, but are not limited to, the use of only authorized entrance and exit points, responsibilities for securing doors and gates, protecting Government property from loss, theft, abuse, or damage, proper use of emergency telephones and challenging persons not displaying required identification badges.  These and other individual security requirements shall be coordinated with the Security and Investigations Division (AMC-700) prior to the start of transition period.

##### 1.6.1.3.1 Contractor Controlled Access

The Contractor shall not permit entrance to locked areas by any person other than contractor personnel engaged in the performance of work in those areas, or personnel assigned to the activity where the contractor is performing work, without written authorization of

the COTR. The CO, COTR, Office of Facility Management (AMP-1) and Security and Investigations Division (AMC-700) personnel, shall have access through any Contractor controlled point providing entry to any Government owned property or facility.

##### Contractor Package Inspection

At the discretion of the Government, any or all Government or personally owned packages, containers, briefcases, purses, etc., brought into, while on, or while being removed from Government property, by the Contractor personnel, are subject to inspection.

##### 1.6.1.3.3 Stolen, Missing, or Damaged Government Property

The Contractor shall report all suspected stolen, missing, or intentionally damaged Government property to the CO and the Security and Investigations Division (AMC-700), using Form AC 1600-5.  The report shall be made within one workday of determination that the item(s) is stolen, missing or damaged.  The Contractor shall cooperate with AMC-700, or other Government investigation services conducting investigations or surveys relating to the disposition or status of Government property.

##### 1.6.1.3.4 Stolen, Missing, or Damaged Personal Property

The Contractor shall report all suspected stolen, missing, or intentionally damaged personally owned property which is determined to be missing, stolen, or intentionally damaged while on or in Government facilities to the CO and the Security and Investigations Division, AMC-700, using AC Form 1600-5.  The report shall be made within one workday of determination.  The Contractor shall cooperate with AMC-700 or other Government investigation services conducting investigations or surveys relating to the disposition or status or personal property on or in Government facilities.

#### 1.6.1.4 Security Inspections

The Contractor shall be subject to recurrent and one-time inspections, surveys, risk analysis, and reviews authorized by FAA directives which are conducted by the Security and Investigations Division, AMC-700.  The Contractor shall cooperate fully with AMC-700 in the scheduling and conduct of such inspections, surveys, risk analysis, and reviews.

#### 1.6.1.5 Compliance with Security Directives

The Contractor shall comply with all other pertinent security directives pertaining, but not limited to, Information Security (Privacy Act information, For Official Use Only information, Proprietary information, Classified information, etc.), Industrial Security, Communications Security, and Physical Security.  In addition, the Contractor shall ensure all contract employees complete the computer based SAVI (Security Awareness Virtual Initiative) training at the beginning of the transition period upon hiring of subsequent employees and to all employees on a recurrent basis at least once a year.

#### 1.6.1.6 Key Control

Procedures shall be implemented to ensure that keys and access cards issued to the Contractor by the Government are not lost or misplaced and are not used by unauthorized persons.  The planned procedures for key/access card control shall be included in the Contractor's Quality Control Plan. Only authorized Contractor employees shall use Keys/access cards issued by the Government.  The Contractor shall prohibit the opening of secured areas to persons other than Contractor employees engaged in the performance of assigned work.

### 1.6.2 Vehicle Registration

The Contractor and Contractor employees utilizing Contractor owned or privately owned vehicles on the MMAC shall meet all Oklahoma Department of Public Safety requirements for operation of motor vehicles.  Upon employment or use of parking areas within MMAC limits, Contractor employees shall register vehicles at Pass & ID, Rm. 151, Headquarters Bldg. and obtain a vehicle decal for display on the vehicle as directed.  The Contractor shall assure that Contractor employees comply with vehicle registration requirements and return vehicle pass/decal to the Pass & ID Office within one working day when an employee is no longer in the service of the Contractor, or upon completion or termination of the contract, whichever occurs first.

### 1.6.3 Smoking Policy

In addition to safety regulations, smoking is regulated by Federal regulations and local policy.  The Contractor shall follow smoking policies in effect, or implemented, at each performance location.

## 1.7 QUALITY

### 1.7.1 QUALITY CONTROL

The contractor is solely responsible for the quality of services provided.  The contractor is also liable for contractor employee negligence, and any fraud, waste or abuse.

The contractor's Quality Control Plan shall ensure that products and services are completed in accordance with ANSI/NCSL Z540-1-1994, Part II, applicable Government regulations and instructions, and meet specified acceptable levels of quality, subject to government approval. The operation of the Quality Control Program must be described in a written plan.

At a minimum, the Contractor's Quality Control plan shall include:

* An internal quality control and inspection system for required services.  The job titles and organizational positions of the individuals who will conduct the inspections must be specified.

- A method to identify deficiencies in products and services that may occur.

- Procedures to correct any deficiency in products or services that may occur.

- A file of information regarding inspection and other quality and internal control actions that documents the purpose of the inspection, the results of the inspection, and any corrective action taken as a result of the inspection.  Upon request, this file shall be made available to the Government during the period of performance.

The plan must be maintained and revised as necessary throughout the life of the contract. In the event of any changes to the Quality Control Plan, a revised copy of the plan must be provided to the CO five working days prior to the effective date of the change.

### 1.7.2 QUALITY ASSURANCE

The Government will monitor the contractor's performance using a  quality assurance surveillance plan incorporating the following:

- Customer Service Action (CSA) – A CSA is a method for FAA customers to report deficiencies in Logistics Center products. CSAs are reported on a FAALC Form 4630-2 (see TE-11) attached to the received defective item. The contractor shall maintain a log of all CSAs and work with the COTR to resolve all problems. The COTR will determine when a defective returned item is considered a contractor warranty item.  The Production Controller will issue an SS job order (see 5.2.2.i) for all CSA work and assign a P-2 priority.

- Timeliness – Turn-around-times (TAT) based on priorities.

- Standards – Reviews traceability Records.

- Quality Control Records – Reviews Contractors Quality Control records to determine if Contractor’s plan is being followed.

The Government reserves the right to review all products and services under this contract, including those developed or performed at the contractor's facilities, to determine conformance with performance and technical requirements. The Government reserves the right to change its inspection procedures at any time.

## 1.8 PERFORMANCE EVALUATION MEETINGS

The Contract Manager and Contractor Quality Control Representative shall meet with the CO and COTR as determined necessary by the CO.  Mutual effort will be made to resolve any and all problems identified.  The Contract Manager or alternates(s) shall meet as necessary with CO and COTR to discuss emergency situations and shall respond within 30 minutes to requests for meetings during normal duty hours and within two hours after normal duty hours.

## 1.9 HOURS OF OPERATION

Normal FAALC operation hours are from 6:00 a.m. to 6:00 p.m., Monday through Friday, excluding Federal holidays. The Contract Manager shall ensure that sufficient contractor employees are present to accomplish the work assigned in this PWS during the core hours of 8:00 a.m. to 4:30 p.m. On occasion work may be required during extended work hours or weekends to meet priorities specified in paragraph 5.2.3.  The Contractor shall inform the COTR when government facilities will be required after normal duty hours or on weekends to accomplish assigned tasks.  The contractor’s work schedule shall be changed only upon prior written approval of the COTR.

### 1.9.1 On-Call Emergency Support

The contractor shall provide on-call emergency support twenty-four hours a day, seven days a week in response to high priority field requirements or any other emergency situation.  The Contractor shall provide a letter of designation to the COTR with name and phone numbers of the primary and alternate points of contact. The contractor shall respond to any inquiry or problem within two hours of initial contact.

### 1.9.2 Federal Holidays

Observance of legal holidays and facility closures.  Generally, the contractor shall not be required to work on Federal holidays or days of Aeronautical Center and/or Logistics Center closings.  The following is a list of Federal holidays and potential closures:

New Years day

Martin Luther King’s Birthday

Presidents Day

Memorial Day

Independence day

Labor Day

Columbus Day

Veterans Day

Thanksgiving Day (AML facilities are normally closed on the day after Thanksgiving requiring Government employees to use one day of annual leave)

Christmas Day

Any other day designated by Federal statute, executive order, or presidential proclamation.

Additionally, local determinations relating to adverse weather conditions, national emergencies, energy conservation, MMAC/ Organizational determinations, etc., may require the Center or the requiring organization (e.g., AML,FAALC) to close.  During such periods of closure, contractor employees will not be allowed to work unless determined "essential" by the COTR; nor will the contractor be entitled to equitable adjustments due to such closures.

## 1.10 CONTINGENCIES

Special situations shall include, but not be limited to, structural fire, accidents, civil disturbances, disaster warnings, acts of God, national emergencies and international crisis which may require that the contractor operate on an extended basis.  The Contractor shall provide these services as requested by the CO.

### 1.10.1 Contingency Plan

The contractor shall develop and maintain a detailed Contingency Plan to be submitted to the CO for approval 10 working days prior to the start of the base year performance period.  The contractor shall be required to update this Contingency Plan annually once contract is awarded.  The Contingency Plan shall include the following:

* 	Contractor's ability to expand the workforce.

*	 Contractor's ability to work at alternate FAA work sites in the

local area.

*	 Contractor's ability to provide work sites and equipment.

(Contractor’s lease expenses to be reimbursed by government.   	  Any alternate work site must meet OSHA and environmental

requirements.)

### 1.10.2 Strike Contingency Plan

The contractor shall develop a strike contingency plan to ensure continuity of operations in the event of strike by contractor personnel. Contractor services under strike contingency plan shall be at no additional cost to the Government.  The Strike Contingency Plan shall be submitted to the CO for approval 10 working days prior to the start of the base year performance period with the final Quality Control Plan.  Any changes to the Strike Contingency Plan shall be provided in writing to the CO within five days prior to the change's effective date.

## 1.11 ENVIRONMENTAL PROGRAMS

### 1.11.1 Regulations/Laws.

The contractor shall comply with all Federal, State and local laws and regulations for standards regarding environmental pollution.  These documents are specified in TE-9.  The contractor shall also comply with all Aeronautical Center policies and procedures relating to environmental compliance, including AC Order 1050.4 Mike Monroney Aeronautical Center Spill Prevention and Response Plan.  All environmental protection matters shall be coordinated, through the CO, with the primary on-scene coordinator.

### 1.11.2 Compliance Requirements

Any of the Government facilities operated by the Contractor may be inspected by the CO or other authorized representatives.

### 1.11.3 Citations

Citations of Government owned, Contractor operated (GOCO) facilities for noncompliance with environmental standards are a matter for resolution between the FAA and the issuing office of EPA or State of Oklahoma regulatory authorities.  Payment of fines or penalty charges associated with citations issued by Federal, State or local officials shall be paid by the Government.  If the citations are issued due to faulty operation or maintenance practices by the contractor, the CO shall deduct the fine from any monies due the Contractor.

## ENERGY AND UTILITIES CONSERVATION PROGRAMS

The contractor shall participate in the MMAC energy conservation program.  Participation shall include taking actions to minimize energy losses.

### Conservation Instruction

### The contractor shall comply with published rules and regulations issued by the U.S. Department of Energy, 10 CFR  Part 490.  The contractor shall instruct personnel in utilities conservation practices, and require them to operate under conditions which preclude waste of Government-furnished utilities.  The contractor's instructions and programs shall include, as a minimum, using installed lights only in areas where work is actually being performed and turning off water faucets, valves and equipment after required usage has been accomplished.  Additionally, the contractor shall ensure controls for heating, ventilation and air conditioning systems are only adjusted by authorized personnel.

## 1.13 ACCESS LIMITATIONS

### 1.13.1 Restricted Areas

The contractor shall comply with restricted area procedures and instructions including proper security clearances.  This includes signing in and out after hours at the Headquarters building for access to LSF/repair shops.  Names of personnel requiring frequent access to restricted areas shall be provided to the CO.

### 1.13.2  "Off Limits" Areas of Facilities

Certain buildings and other facilities are "off limits" to the general public.  Contractor personnel shall not enter any "off limits" facilities without specific written permission from the CO.

### 1.13.3 Interference with Contractor Performance

In the event anyone other than the CO or his/her authorized representative requests the contractor to temporarily cease work in an area, the contractor shall immediately report the instruction to stop work, including the name of the person directing the work stoppage, to the COTR.

## 1.14 INSPECTION BY REGULATORY AGENCIES

The contractor shall notify the CO by phone immediately upon arrival of any inspection visit by an agent or agents of any regulatory agency.  The contractor shall submit a copy of any reports received to the CO within 1 working day.

## 1.15 SAFETY REQUIREMENTS AND REPORTS

All work shall be conducted in a safe manner protecting the environment and shall comply with:

a.  29 CFR 1910 OSHA Standards (General Industry).

b.  29 CFR 1926 OSHA Standards (Construction).

c.  National Fire Protection Association (NFPA) National Fire	  			       Codes, and updates thereto.

d.  American National Standards Institute (ANSI) Safety

Standards (latest versions) as applicable.

e.  FAA Order 3900.19B (and updates) Occupational Safety

and Health.

f.  AC Order 3900.21F (and updates) Occupational Safety.

g.  FAA Order 1900.1F (and updates) FAA Emergency

Operational Plan.

h.  AC Order 1900.12A (and updates) Aeronautical Center

Emergency Operations Plan.

- FAA Order 1050.10C (and updates) Protection Control and

Abatement of Environmental Pollution at FAA facilities.

j.  40 CFR Parts 101400 EPA Regulations.

If the contractor fails or refuses to comply promptly with environmental or safety requirements, the CO may issue an order stopping all or part of the work until satisfactory corrective action has been taken.  No part of the time lost due to any such order shall be made the subject of claim for extension of time or for excess costs or damages to the Government.  The contractor shall be responsible for enforcement of all environmental and safety requirements by the contractor personnel and his subcontractors.  The contractor shall include a clause in all subcontracts to require subcontractors to comply with the environmental and safety provisions of this contract, as applicable.  The contractor shall immediately secure any accident scene and wreckage until released by the accident investigative authority through the CO.  If the Government elects to conduct an investigation of any incident, the contractor shall cooperate fully and assist the Government personnel until the investigation is completed.

Safety and health standards consistent with requirements of the Occupational Safety and Health Administration (OSHA) shall be maintained.  Compliance with the environment regulations issued by the U.S. Environmental Protection Agency (EPA), the Oklahoma Department of Environmental Quality (ODEQ) or other authorized agency shall be maintained.  The Department of Labor (DOL), EPA, ODEQ and any other authorized agency upon receiving right of entry from the Environmental, and health Staff, AMP-100A, has statutory authority to inspect all places of employment occupied by the contractor.  Citations against the contractor for noncompliance with OSHA standards, EPA, ODEQ or other regulations are a matter for resolution between the Contractor and the issuing agency unless non-compliance is the result of Government-furnished property or facilities which were in non-compliance when furnished to the Contractor.  Resolution of any problems of this sort will be handled by the CO and the contractor.  Close liaison shall be established and maintained with Government safety and environmental representatives to ensure that working conditions provide an optimum degree of safety for both contractor and Government personnel and environmental protection.  The Government reserves the right to inspect the contractor’s operations, conduct and investigate the incidents occurring as a result of contractor's operation in which there is damage to Government-furnished items, or injury or occupational illness involving Government or contractor personnel or environmental impact.

### 1.15.1 Accident Reporting

The contractor shall comply with all EPA, OSHA requirements for record keeping and reporting of all incidents resulting in death, serious injury, occupational disease, or adverse environmental impact.  The contractor shall provide a verbal report to the CO immediately after each such occurrence.  A completed typed original mishap report in accordance with FAA Order 3900.1B shall be delivered to the CO within 48 hours of occurrence.

## 1.16 TRANSITION REQUIREMENTS

This contract contains transition requirements which must be accomplished in accordance with an FAA approved transition plan.  The transition plan shall be submitted for FAA approval at time of submission of contractor’s Technical Proposal. The purpose of the plan is to assure continued Test Equipment support without interruption.  Consequently, it is imperative that transition from incumbent contractor to full contract performance be accomplished in a well-planned, orderly and efficient manner.  The contractor’s transition plan shall include a provision for the contractor to receive, during the transition period, all work in process which cannot be completed by the incumbent contractor prior to contract start-up and which cannot be postponed.  This action is to enable the contractor to plan, estimate, and obtain the material and personnel resources to perform all work.  The contractor shall not assume that incumbent contractor employees will be available to guide, direct, or specifically orient each contractor employee.   The contractor shall cooperate with the incumbent during the transition period and shall conform to the transition plan developed by the contractor and approved by the Government.  Certain Government staff will be available during this period to provide administrative and technical orientation to contractor personnel, familiarize contractor with required services, and provide other guidance and assistance as mutually determined by the Government and the contractor.  Contractor personnel will be required to obtain security badges during the transition period.

### 1.16.1 Transition Period

The transition period is tentatively scheduled to begin on 1 September 2006, 30 days prior to start of base year period.

### 1.16.2 Phase-Out

At the conclusion of any performance period, including option periods or extensions, the services provided under this contract may be awarded to another contractor.  The incumbent contractor shall be required to assist in transition activities.

## 1.17 PWS Reference Information

This PWS references many volumes of information.  This information is to be considered as an appendix to this solicitation.  The referenced information consists of several collections of documents which can be obtained from the COTR, Operational Services Branch, AML-4010.  TE-9 FAA Applicable Documents and TE-10 Required Reports/Plans provide quick references to necessary FAA regulations and required reports.

S E C T I O N  C - 2

# C-2 DEFINITIONS

ADJUST:  To mechanically or electrically change within allowable tolerances in order to match, fit or bring into proper relationship.

ANCILLARY EQUIPMENT:  Plug-in units, printed circuit cards, etc. without which the workload item is not complete as required for the assigned national stock number (nsn).

CALIBRATION:  A comparison between two instruments, one of which is a standard of known accuracy, to detect, correlate, and adjust.

Note: Replacement of batteries (9 volt, C, D, AA, and AAA) in small hand held test instruments such as DMMs, meters and analyzers, etc. do not constitute a repair. The contractor shall replace these batteries during normal calibration as required and will be paid under the normal CLIN “A” rate. The government will provide the contractor with a sufficient stock of these type of batteries. rechargeable batteries, specialized batteries and battery packs shall be purchased by the contractor and will be paid under the appropriate CLIN “B” repair rate.

CANNIBALIZATION:  The removal of a part(s) from one end item in order to fill a parts requirement in another end item.  Removal of the part renders the original end item incapable of performing its designed function.

CHECK:  To examine, test, or compare with a standard to verify that the unit under surveillance operates within design specifications.

CERTIFICATION:  The act of designating that standards and precision measurement equipment have been calibrated and meet established technical requirements.

CIRCUIT CARD ASSEMBLY (CCA):  A nonferrous card with printed or etched circuits and attached electronic components that perform an electronic function or group of electronic functions.

COMPONENT:  A part of an overall equipment or system including  minor bits and pieces.

CONTRACTING OFFICER (CO):  The person authorized to act on behalf of the Government to negotiate and award contracts and modifications thereto, and to administer contracts through completion or termination.  Except for certain limited authority delegated by the CO to a technical representative, the CO is the only individual with the authority to direct the work of the contractor.

CONTRACTING OFFICER TECHNICAL REPRESENTATIVE (COTR):  The authorized Government representative(s) acting within the limits of their delegated authority for management of specific projects or functional activities.

CONTRACTOR:  The term Contractor as used herein refers to both the prime Contractor and any Subcontractors.  The prime Contractor shall be responsible for ensuring that Subcontractors comply with the provisions of the contract.

CO-UTILIZED EQUIPMENT:  Government owned equipment (GFE) that shall be used jointly by the Government and the Contractor.

CUSTOMER SERVICE ACTION (CSA): A CSA is a method for FAA customers to return damaged, defective, or misidentified products to the Logistics Center and is tracked on an FAALC Form 4630-3.  See TE-11 for example form.

DELIVERABLE:  Any reports or forms supplied by the Contractor to the Government to perform data required by the PWS.

EMERGENCY WORK:  Work which takes priority over all other work orders and requires immediate action including diverting personnel from other jobs, if necessary, to cover the emergency.

EXPENDABLE PROPERTY:  Government property that is consumed in use or loses its identity in use and is dropped from stock record accounts when issued or used.

FACILITY:  Any building, plant, installation, structure, location, or site of operations in the performance of a contract or subcontract.

GOVERNMENT-FURNISHED EQUIPMENT (GFE):  Government owned equipment (GFE) provided to the Contractor for use in fulfilling the terms of this contract only.

GOVERNMENT-FURNISHED MATERIAL (GFM): All material provided by the Government for the exclusive use of the Contractor in fulfilling the terms of this contract only.

GOVERNMENT-FURNISHED PROPERTY (GFP):  All equipment, facilities and material provided by the Government for the exclusive use of the Contractor in fulfilling the terms of this contract only.

GOVERNMENT REPRESENTATIVE:  The Contracting Officer (CO), Contracting Officer Technical Representative (COTR), Quality Assurance Evaluator (QAE), Center Safety and Environmental personnel.

INSPECTION:  The comparison of product or service against contract requirement in order to establish conformance or nonconformance with the contract requirements.

MAINTENANCE (GENERAL):  The work required to preserve and maintain equipment and material in such condition that it may be effectively used for its designated functional purpose.

MATERIAL:  Property that may be incorporated into or attached to a deliverable end item or that may be consumed or expended in performing the contract.

METROLOGY:  The science of measurement used to determine conformance to technical requirements.  Includes developing standards and systems to be used in making absolute and relative measurements.

MODIFY:  To change or alter the original fit, form, or function of an item.

NATIONAL AIRSPACE SYSTEM (NAS):  System for modernizing and improving

air traffic control and airway facilities services.

PART:  A general term meaning any component, minor bit and piece, circuit card assembly, line replaceable unit, subassembly or assembly.

PERFORMANCE DATA RECORD:  A record of the minimum performance requirements and the calibration standards used to calibrate and certify a workload item.

PERFORMANCE WORK STATEMENT (PWS):  A document that describes the requirements, material, or services, including the performance standards for contractible services.

PERSONAL PROPERTY:  Property of any kind except real property or records of the Federal Government.

PRECISION MEASUREMENT EQUIPMENT:  Test and measurement equipment used to measure, calibrate, gauge, test, inspect, diagnose, or otherwise examine material, supplies, and equipment to determine whether they comply with technical documents, such as engineering drawings, technical orders, or military standards and specifications.

QUALITY ASSURANCE (QA):  A method used by the Government to check goods or services to determine whether or not they meet the requirements of the contract.

QUALITY ASSURANCE SURVEILLANCE PLAN (QASP):  A written plan that details what is to be evaluated, how evaluations are to be accomplished, frequency of evaluations, and evaluation parameters.

QUALITY CONTROL PROGRAM (QCP):  Contractor's system to control the equipment, systems, or services to assure that requirements of the contract are performed.

REPAIR (GENERAL):  The restoration of an item to its original fit, form, and function so that it may be efficiently used for its designed purpose.  Work includes replacement of defective or worn components, replacement of broken appendages, re-soldering, etc.

RESIDENT ALIEN:  An individual admitted by the U.S. Immigration and Naturalization Service (INS) for permanent residence, and who holds INS Form I-151 or INS Form I-551 (green card).

RTO (Return to Owner): status of customer’s equipment, usually IP, IE, or RR that is returned un-repaired due to unavailability of part(s) or beyond economical repair condition.

SCHEDULED WORK:  That work which is identified as controlled by the Contractor on a routine daily basis without direction from the CO.

SERVICEABLE ITEM:  An item that has been repaired and/or calibrated and certified to be free of defects or malfunctions, and is mission capable.

SHOP STOCK:  Parts consumed in daily operation and maintenance work that are kept in the various maintenance shops.

SPECIAL TEST EQUIPMENT:  Either single or multipurpose integrated test units engineered, designed, fabricated, or modified to accomplish special purpose testing in performing a contract.

STANDARD:  An acknowledged measure of comparison.

SUBASSEMBLY:  A functional grouping of circuit card assemblies and/or line replaceable units together with a mounting circuit board (mother board or back plane) and mounting hardware such as drawers, boxes, etc.

SURVEILLANCE:  Planned or random observations of the timeliness, accuracy, completeness and/or quality of services performed.

SURVEY:  An item that is either no longer used in the NAS system or is beyond feasible or cost effective repair and as such made available for disposal.

TECHNICAL EXHIBIT (TE):  A document furnished as an aid to further define elements of the PWS.

TEST:  An operation under fixed conditions compares actual performance to design standards and issued to verify serviceability and to detect malfunction or failure by use of test equipment or other methods.

TURN AROUND TIME:  Turn around time shall start as "Day Zero" when the Contractor receipts the Government for the workload item to be serviced.  The turn around time is concluded upon Contractor getting receipt from the Government scheduler indicating that the total contract services have been completed.

WORKAROUND:  An alternate method or approach to accomplishing work when the primary method or approach is temporarily suspended due to an identified hazard which precludes or limits the normal work process from occurring.

WORK ORDER:  Document authorizing, directing or requesting maintenance, repair, modification, fabrication or engineering services.  May include a single process, a group of processes, a single item, a group of items, or any combination thereof.

# C-3   GOVERNMENT-FURNISHED PROPERTY AND SERVICES

The Government will provide without cost to the contractor the property and services indicated below.  The Government-furnished property (GFP) and services provided as part of this contract shall be used by the contractor only to perform under the terms of this contract.  The government has provided sufficient GFP, specifically test equipment standards to perform the majority of the work provided in this contract. Occasionally newly acquired equipment or unique instruments may be submitted to be worked through the test equipment work center where the appropriate standard may not be available as Government furnished. The contractor may under these circumstances provide their own standards, subcontract the work, or submit a request through the COTR to procure the required standard(s). The COTR will have the discretion to determine if procuring the standard(s)is in the best economical interest of the government. Also see paragraph 3.5.7 and section C-4.

## 3.1 EQUIPMENT AND INSTALLED PROPERTY

The Government will provide the equipment identified in Technical Exhibit 6 and installed property/facilities shown in Technical Exhibit 8.  The GFP shall not be removed from the MMAC without prior written consent from the CO.  GFP shall be managed and accounted for in accordance with the Government property clause of this contract.

## FACILITIES

The Government will furnish the facilities shown in TE-8.  There may be joint use of facilities by both Government and Contractor personnel.  The Government will provide maintenance on Government-furnished facilities.  No alteration to the facilities shall be made by the contractor without specific written permission from the CO.

Facilities have been inspected for compliance with Occupational Safety and Health Administration (OSHA) standards. No hazards have been identified for which workarounds have been established.  The Government corrects OSHA hazards in accordance with center wide Government developed and approved plans of abatement taking into account safety and health priorities.  A higher priority for correction will not be assigned to the facilities provided hereunder merely because of this contracting initiative.  The fact that no such conditions have been identified does not warrant or guarantee that no possible hazard exists, or that workaround procedures will not be necessary or that the facilities as furnished will be adequate to meet the responsibilities of the Contractor.  Compliance with OSHA standards and other applicable laws and regulations for the protection of employees is exclusively the obligation of the Contractor, and the Government will assume no liability or responsibility for the contractor's compliance or noncompliance with such responsibilities, with the exception of the aforementioned responsibility to make corrections in accordance with approved plans of abatement subject to center wide priorities.

Prior to any modification of the facilities performed by the contractor, the contractor must notify the CO and provide documentation describing in detail the modification requested.  No alterations to the facilities shall be made without specific written permission from the CO; however, in the case of alterations necessary for OSHA compliance, such permission shall not be unreasonably withheld.

## 3.3 GOVERNMENT-FURNISHED MATERIAL (SHOP STOCK)

The Government provided an initial inventory of material

(approximate 30 day stock level) to perform the work identified in this PWS during the initial contract in January 1992 and subsequently maintained by the incumbent contractor.  The contractor shall maintain a sufficient 30 day level at his expense to repair the many common failures, e.g., fuses, lamps, feet, transistors, diodes, fans, switches etc., to preclude unnecessary delays in established priority times.  These materials shall be jointly inventoried at the start of the transition period by the contractor and Government representative.  The resulting inventory shall ensure that the incumbent contractor provides an adequate 30-day level of materials at the end of the performance period to be provided as GFM to successor contractor.  TE-3A lists the average 30 day parts used and TE-3B list all parts used in FY-05.

## 3.4 DOCUMENTS AND FORMS

Government forms, regulations, and directives will be furnished by the Government, except as indicated in section C-6.  Initial supplies of these items will be available at the start of the transition period.  The contractor shall establish requirements for subsequent needs, prepare requisitions for such requirements and submit them to the COTR.

## 3.5 ACCOUNTABILITY FOR GOVERNMENT-FURNISHED PROPERTY

The following paragraphs apply in total to Government-furnished property intended for use by the contractor.  The Government reserves the right of access to the Government-furnished property.  Contractor liability for joint use property will be restricted to validated damage, theft, or negligence attributed to action or nonaction of the contractor.

### 3.5.1 Property Control Procedures

The contractor shall conform to the requirements of the Acquisition Management System (AMS) 3.10.3 concerning management of Government-furnished property (refer to http://fast.faa.gov/index.htm) The contractor is directly responsible and accountable for all Government property in his possession during performance of this contract.  Adequate property control records must be maintained by the contractor's property control manager.  The contractor shall prepare and submit draft property control procedures to the COTR within 30 days after award of the contract.  These procedures must be approved by the COTR pursuant to the terms of the contract.

### 3.5.2 Initial Government-Furnished Property Inventory

During the transition period, the contractor and the COTR (or their designees) shall conduct a joint inventory of Government-furnished property.  The contractor shall provide a receipt for property provided by the Government.  The contractor and a Government representative shall jointly determine the working order and condition of the equipment.  Items of property missing or not in working order shall be reported to the COTR within 10 days of completion of the initial inventory.  The Government will replace or repair any missing or defective Government-furnished property necessary for accomplishment of work discussed in this PWS.  The CO (or designee) will provide disposition instructions for items beyond repair.  The contractor and the COTR shall certify their agreement on working order and discrepancies in a written report to the CO.  If an irreparable item is to be returned to FAA, the contractor shall complete AC Form 4100-301-2 FAA Condemned Part Tag, (see TE-11) which will accompany the irreparable Government-furnished item.

### 3.5.3 Government Furnished Equipment Warranties

The COTR will provide the contractor all existing manufacturer's warranties on GFE at the start of the transition period.  The contractor shall exercise these manufacturer's commercial warranties on GFE.  The contractor shall report to the CO any difficulty in exercising manufacturer warranties and request assistance as necessary.  The contractor shall provide to the COTR the original warranties on new equipment received or installed.  These warranties shall be made out to the Government.  Government equipment installed by the contractor that fails within a warranty period due to contractor's poor workmanship, or by not following manufacturer's installation, operation, or maintenance instructions, shall be replaced or repaired at the Contractor's expense.  This determination will be made by the CO.

### 3.5.4 Annual Inventory

The contractor shall inventory all material and equipment, identified in TE-6 at least once each year during the third quarter of the fiscal year.  Since the FAA Property Administrator (the COTR) will normally participate in the inventories, the contractor shall coordinate with the FAA Property Administrator before taking an inventory.  Throughout the performance period, the contractor shall ensure that the equipment inventory listing for the FAA approved system is current, complete and accurate.  Any unused GFE should be turned in to the FAA Property Administrator during the inventory.

### 3.5.5 Phase-Out Inventory of GFE

At completion of the performance period, a joint inventory of property shall be conducted by the contractor and the CO (or their designees).  The contractor shall be liable for loss or damage to Government-furnished property beyond fair wear and tear in accordance with the clause of the contract, "Government -Furnished Property".  Compensation for replacement of lost property or property damaged beyond fair wear and tear shall be affected either by withholding amounts owed to the contractor or by direct payment by the contractor; the method of compensation will be determined by the CO.  In the case of damaged property, the amount of compensation due the Government by the contractor shall be the actual cost of repair, provided such amount does not exceed the replacement cost of equipment.  For items lost or damaged beyond economical repair, the amount of the contractor's liability shall be the depreciated replacement value of the item.  Determinations of economical repair and replacement values shall be provided by the CO.  Any failure of the contractor to agree with such determination shall be treated as a dispute over a question of fact pursuant to the clause of this solicitation entitled "Disputes".  All Government-furnished equipment shall be returned to the Government in the same working condition as received, including current calibrations on all Government-furnished test equipment.

### 3.5.6 Disposition of Property

When property is determined, by joint agreement between the contractor and the CO to be beyond economical repair (see paragraph. 5.2.5.2.3 for determination process) or becomes obsolete, or replaced, the property will be returned to the Government in its entirety.  Upon completion of the performance period, remaining Government property shall be returned to the Government.

### 3.5.7 Obtaining Additional GFE Property

The contractor shall submit requests for additional Government-furnished equipment required in the performance of this contract, with adequate justification to the COTR.  The COTR in consultation with the contractor, shall determine the legitimacy of the request.  The contractor shall be responsible for meeting the requirements of the PWS even if additional GFE is not provided.

### 3.5.8 Equipment Repair

The contractor shall be liable for loss or damage to Government-furnished equipment beyond fair wear and tear in accordance with the terms of the contract.  The Government will provide routine maintenance and repair of Government-furnished administrative office equipment; i.e., PCs, office furniture, typewriters, copiers, etc.  The contractor shall perform routine calibration, maintenance, repair, and modification on all other Government-furnished property at no additional cost.  All equipment in need of calibration/repair/ maintenance shall be calibrated/repaired/ maintained by the contractor within 30 days of discovery, but before the annual inventory is conducted.  All calibrations/repairs/maintenance not performed by the contractor which are determined necessary by the Government shall be accomplished by the Government at contractor expense.  In the case of damaged property, the amount of compensation due the Government by the contractor shall be the actual cost of repair.  Failure of the parties to agree on repair costs shall be treated as a dispute under the "Disputes" clause of the contract.

### 3.5.9 Replacement of Equipment

The Government will replace, as required, the equipment listed in TE-6.  However, the Government is required to replace such equipment only when due to fair wear and tear, and no longer usable for its intended purpose.  Equipment is determined no longer usable when the repair cost of equipment is greater than or equal to 75% of the unit price.  The contractor shall submit requests for replacement of GFE required in the performance of the contract to the COTR.

### 3.5.10 Applicable Manufacturer's Literature

Equipment operating and maintenance manuals and supplier's catalogs presently available will be turned over to the contractor at the start of the transition period.  A complete listing of all operator/maintenance manuals is shown in TE-7.  The contractor shall be responsible for updating this listing as required in same or compatible format.  The contractor shall be responsible for the upkeep of all manuals and will be required to replace those damaged due to negligence.  The FAA will provide new manuals as needed.  An inventory of suppliers' catalogs will not be taken since the catalogs are a disposable item and become obsolete.  The contractor shall be responsible for obtaining and updating catalogs as new issues are published by suppliers.

The contractor shall maintain an up-to-date supplier catalog file of pertinent supplies and components for Government-furnished equipment maintained under the contract.  These documents shall become the property of the Government at the expiration or termination of the contract.

### 3.5.11 Damage Reports

In all instances where Government property or equipment is damaged by contractor's employees, the Contractor shall provide a verbal report to the CO within 4 hours of occurrence.  Two typed copies of the report shall be delivered to the CO within 24 hours of occurrence, explaining the circumstances of the accident and the extent of damage.  Liability for loss or damage and cost for repair or replacement of Government property, shall be governed by the Government-furnished property clauses specified in the contract.

## 3.6 SERVICES.

The Government will furnish the following services at no cost to the Contractor except as otherwise stated.

### 3.6.1 Utilities

Utilities (electricity, water, sewer & heat) shall be furnished to the Contractor without charge from existing outlets and supplies.

### 3.6.2 Custodial

Custodial services shall be provided to maintain and clean the common areas only.

### 3.6.3 Copier Equipment and Supplies

The Government will provide access to copier equipment and supplies for PWS related Government business only.

### 3.6.4 Postal

The contractor is responsible for obtaining a post office box for incoming mail at the MMAC Post Office.  In the event the MMAC Post Office is unable to provide this service, it is the contractor’s responsibility to obtain a post office box at another USPS location.  The contractor shall be responsible for all mail pick up and delivery.

### 3.6.5 Telephone Services

The Government will provide existing local and Federal Telecommunications System (FTS) telephone service and telephone equipment to contractor personnel.  The contractor shall use Government provided telephone service only for official business.  The Government telephone service shall not be used for personal or other business not related to this contract.  Contractor personnel shall not relocate government-furnished telephone equipment or in any way tamper with the telephone distribution systems.  The contractor shall notify the COTR when relocation, maintenance, or repair of telephones is required.

### 3.6.6 Real Property Maintenance

The Government will provide maintenance and repair of real property facilities.

### 3.6.7 Center Civil Engineering

The Government will provide fire prevention and protection, inspection and maintenance of Government-furnished fire extinguishers and systems, pest control, and grounds maintenance.

### 3.6.8 Security Services

The Government will provide general on/Center Security service.  Security phone extension is 954-3444 for emergencies, and 954-3212 or 954-4566 for routine calls.

# C-4 CONTRACTOR FURNISHED PROPERTY

The Contractor shall furnish the property necessary to perform the services required under this contract not specifically supplied by the Government in Section 3.

## 4.1 PROPERTY

Contractor furnished vehicles and equipment shall be identified as contractor property.  All contractor furnished vehicles and equipment shall be in an operable condition and meet all local, State, and Federal safety requirements, and requirements of 40 CFR 243.  Vehicles and equipment identified as not meeting the above safety requirements, by inspection by the COTR, shall be removed from service within 1 hour of notification and repaired or replaced at contractor's expense.  Except for minor on site repairs, the contractor shall remove from MMAC, within 24 hours, any vehicle which becomes inoperative or which breaks down during operation.

## 4.2 ADMINISTRATIVE SUPPLIES

The Contractor shall provide all day to day administrative supplies i.e., pens, paper, folder, binders, etc., required for compliance with the requirements of this contract.

## 4.3 TOOLS

The contractor shall provide all necessary hand tools to perform maintenance, repair, modification, calibration, etc. required for compliance with the requirements of this contract.

## TEST EQUIPMENT

Any test equipment the contractor provides to supplement the GFE shall be that which is recognized as standard in the trade.  The contractor equipment used shall be calibrated and certified IAW criteria established in ANSI/NCSL Z540-1-1994.  The contractor shall furnish to the CO two weeks after equipment is acquired, a list of all test equipment and a proper certification that all test equipment has been calibrated.  This contractor furnished equipment shall not be used for calibrations or certifications without the approval of the COTR.

## FUELS

The Contractor shall be responsible for furnishing vehicle and equipment fuels for Contractor owned vehicles and equipment.

## 4.6 MATERIAL AND PIECE PARTS

The contractor shall ensure that the Government Furnished Material (GFM) specified in section 3.3 is maintained at a 30-day level of supply at all times.  This parts supply is intended to preclude unnecessary delays in the performance of repairs in order to meet assigned priorities. The Government realizes that it is impossible to maintain all possible parts expected to fail, yet a reasonable effort shall be made to maintain a stock of parts which often fail. The material and piece parts requirements will change with ongoing upgrade of FAA Test Equipment.  The contractor shall continually assess the types and models of assets maintained in order to properly adjust requirements for performance of the PWS.  This 30-day level of supply shall become the property of the Government at the end of the performance period to provide continuous performance of either government or successive contractor service.

## 4.7 PERMITS

The contractor shall, at no additional cost to the Government, obtain all appointments, licenses and permits required for performance of work and for complying with all applicable Federal, State and local laws.  Permits and licenses shall be obtained prior to start of base year and kept current throughout the contract period.

## 4.8 CUSTODIAL SERVICES

The contractor shall be responsible for custodial services in areas occupied.  The contractor shall dust, sweep, mop and empty trash cans as needed to maintain a neat, clean and safe working environment.  The contractor shall ensure that a work area is maintained in safe condition during work activities at locations other than the facilities listed in TE-6.  The contractor shall ensure upon completion of the work that the work area is left in a condition of cleanliness and safety.  This shall be the same condition or an improvement of the work area condition prior to the commencement of the work.

# C-5 SPECIFIC TASKS

## 5.1 GENERAL

The Test Equipment Activity shall operate in accordance with the guidelines of ANSI/NCSL Z540-1-1994 and other applicable approved standards.  The Test Equipment Classification for Bid exhibits, TE-1A and TE-1B; Workload Projections, TE-2A; Parts Utilized, TE-3; Obsolete Parts, TE-4; provide historical data from FY-05.  All exhibits are designed to give the prospective contractor a historical basis of information only and should be understood that future equipment requirements will change.  The tasks in this section apply to all services required under this contract.  Test Equipment Repair and Calibration Services specific tasks are defined in section 5.2.  These services shall be performed in accordance with all laws, standards, DOT and FAA instructions as specified herein and referenced in section 6 and TE-9.

### 5.1.1 Work Management

The contractor shall plan, program, coordinate, estimate, schedule, evaluate resources and execute work assignments.  Work management shall include maintaining a suspense system to meet the timeliness requirements of all assigned work.

### 5.1.2 Budget Preparation

The contractor shall participate in the preparation/development of budget requirements for new or replacement GFE as requested by the COTR. Preparation shall include providing a list of recommended new/replacement GFE along with sufficient justification.

### 5.1.3 Records and Filing Systems.

#### 5.1.3.1 Records

Complete and accurate operating, maintenance and repair records shall be maintained by the contractor as required by this PWS.  The records shall be retained until completion of the contract.  Upon contract completion, the Government will direct the contractor as to which records shall be turned over to the Government and which records may be destroyed.  All records are subject to Government review at any time.

#### 5.1.3.2 Filing System-Work Orders

The contractor shall maintain files for each individual work order, AC Form 6000-11, production order and/or other work assignment documents.  These files shall be maintained in numerical sequence by individual work order number, as identified on each document.  One legible copy of each work order shall be submitted to the COTR upon completion of work. Individual files shall contain copies of any material receipts, delivery orders, sales slips, invoices, etc., relating to the work order.  The contractor shall provide the Government access to contractor maintained files during the term of the contract. All individual or project work files are the property of the Government and shall be turned over to the Government upon completion or termination of the contract.

### 5.1.4 Reports

The contractor shall furnish to the Government all reports and/or forms necessary to perform the data described herein and listed in TE-10.  Any mandatory or requested reports shall be submitted in a format compatible with Government software.  Unless otherwise specified, 2 copies of each deliverable shall be provided to the CO.

## 5.2 TEST EQUIPMENT REPAIR AND CALIBRATION SERVICES

### 5.2.1 In-processing Equipment

The contractor shall take physical custody of all workload items and acknowledge receipt of the workload item by signing, dating, and returning a copy of AC Form 6000-11 to the Production Controller within four hours of delivery.  The contractor shall perform visual inspections on all in-processed items to ensure the AC Form 6000-11 data matches the item.  Each item shall be matched to documentation for proper nsn, part number, options, serial number, etc. and separate workload items accordingly.  Upon discovery of misidentified serial numbers the contractor shall annotate the production order with the correct serial number. Any other misidentification, such as wrong nsn, part number, or option, the contractor shall annotate AC Form 4630-30 Nonconforming Product form and notify the COTR or Production Controller. See TE-11.

### 5.2.2 Workload Programs

The contractor will be able to identify all workload items to the following program codes as annotated in the block "code" of the Production Order, block “1” AC Form 6000-11, or other form(s) as specified accompanying the workload item. The contractor shall maintain serial number control of all workload items. Technical Exhibit 2A provides the government’s best estimate of projected workload for these programs:

a. EQ; Equipment Quality; Quality inspections to validate equipment meets manufacturer specifications upon return from manufacturer(s) and/or vendors. Normally paid at Clin A rate.

b. ER; Exchange and Repair; the exchange of an unserviceable item for a serviceable like item. The contractor shall clean, repair, modify as required and calibrate/certify and provide forward and reverse traceability on all ER program workload items and maintain serial number control. Normally paid at the CLIN B rate.

The COTR orders routine repairable ER work in order to maintain and

replenish FAALC serviceable stock levels.  The contractor shall

maintain sufficient serviceable stock levels as designated by the

COTR and the COTR may assign a higher priority to this normally

routine work when circumstances dictate or when the contractor has

not sufficiently maintained serviceable stock levels.

c. FE; Facilities Equipment: Facilities Equipment requiring inspection for completeness and/or operation.  Items may require inspection, calibration, or return to manufacturer under warranty. The contractor shall perform the tasks described on the AC Form 6000-11-7. The specific FE task assigned will determine the CLIN A, B, or 10 rate.

d. IE; In-use Repair Equipment; Test Equipment at the MMAC that requires repair.  The contractor shall clean, repair, modify as required and calibrate/certify workload items in the performance of the IE Program and maintain serial number control of these items. When IP coded work cannot be calibrated and requires repair, the IP is then recoded as an IE task. The technician shall inform the Production Controller immediately upon discovery that the IP requires repair in order to be issued an IE job order number. The IE start time begins immediately upon change to the IE code.  Paid at the CLIN B rate.

e. IP; In-house Calibration Program; Test Equipment at the MMAC subject to recall for calibration.  The contractor shall clean, calibrate, certify, and provide forward and reverse traceability on all IP program workload items and maintain serial number control.  Paid at the CLIN A rate.

f. RR; Repair and Return of an unserviceable item which normally will have been coordinated with the item manager to ensure this facility has the capability to perform required maintenance.  When there is no serviceable stock available or the LSF does not stock the item, the customer may return their unit to the FAALC for repair and subsequent return to using facility. The contractor shall clean, repair, modify as required and calibrate/certify workload items in the performance of the RR Program and maintain serial number control of these items. Occasionally an RR may be returned for calibration only. Paid at the CLIN A or B rate.

g. SP; Special Facilities Equipment requiring inspection for completeness and/or operation.  Items may require calibration, repair, or return to manufacturer. The contractor shall perform the tasks described on the AC Form 6000-11-7. The specific SP task assigned will determine CLIN A, B, 10 rates.

h. SS; Supply Support; Special tasks which may include calibration, certification, inspection, modification, sorting, warranty returns,  test for serviceability, and evaluation. Most SS work will be inspection and calibration of serviceable assets prior to shipment.  The contractor shall perform the tasks described on the AC Form 6000-11 or FAA Form 4250-4 Shipping Order in performance of the SS Program.  The specific SS task will determine CLIN A, B, or 10 rates.

i. CSA (Customer Service Action); Failed and/or incorrectly ordered equipment will normally be returned to the Logistics Center via the CSA program and in-turn routed through the test equipment work center. Items that the customer may have mistakenly ordered are also returned and routed through the test equipment work center to determine its condition, functionality and certification status. CSAs must be treated with the utmost urgency in order for FAA customers to be properly credited or billed for returned assets, therefore, all CSAs shall be assigned a P1 priority. Any CSA item received with missing or broken cal void labels shall void any FAA or contractor warranty. The contractor shall notify the COTR for verification immediately upon receipt of any asset having broken or missing labels. The COTR and the contractor’s quality representative shall perform a joint inspection of returned warranted items. Normally, only the contractor’s calibrations and specific repairs shall be warranted unless determined by joint review that something should have been repaired/replaced that was not.  The COTR will determine if the failed item was due to any contractor oversight or negligence.  The contractor at no additional cost to the Government shall rework any returned item which the COTR determines to be the contractor’s responsibility within the stated warranty period(s). CSAs are issued on SS job order numbers.

j. Surveys and RTO’s(Return to Owner): When repairs cannot be completed and result in a survey or RTO, the contractor shall be credited for up to two hours of the attempted repair under CLIN 12. See paragraph 5.2.5.2.3.

### 5.2.3 Workload Priorities and Turn Around Times (TAT)

The contractor shall meet the specified turn around times (TAT) in calendar days for each assigned priority on all workload items.  Turn-around times are measured from the time the contractor acknowledges receipt of an item by signing and dating the applicable work order document until completion when the work order document is submitted to the COTR for completion acknowledgement. The COTR may change the priority status of any workload item at any time to meet mission requirements.  Priorities may require additional emphasis beyond the normal shift schedule. See TE-2B for numbers of workload by priority for FY-05.

a. P1-SS (1 day): The contractor shall start work immediately upon receipt of any shipping order FAA Form 4250-4(a) and continue work until completion. The P1-SS takes precedence over all other priorities. The P1-SS may require interruption of lower priority workload and completed no later than one day from issuance.

b. P1-all other (3 days): The contractor shall start work immediately upon receipt of asset and AC Form 6000-11 and continue work until completion.  P1’s may require interruption of lower priority workload.  All P1’s shall be given the utmost urgency and completed no later than 3 calendar days from issuance.

c. P2 (5 days): The contractor shall start work upon receipt of asset and AC Form 6000-11.  P2’s may require interruption of lower priority workload.  All P2’s shall be given an urgency just below that of P1 and completed no later than 5 calendar days from issuance.

d. P3 (10 days): The contractor shall start work upon receipt of asset and AC Form 6000-11.  P3’s may require interruption of lower priority workload.  All P3’s shall be given an urgency just below that of P2 and completed no later than 10 calendar days from issuance.

e. P4 (due date): The contractor shall start work upon receipt of asset and AC Form 6000-11.  The COTR will assign a due date based on the customer’s requirement. The due date may be as early as 1 day. P4’s may require interruption of lower priority workload.   All P4’s shall be given appropriate urgency based upon the due date.

f. P5 (30 days): The contractor shall start work within a time frame to allow for completion no later than 30 calendar days from receipt of asset and AC Form 6000-11.  P5’s will be issued to fulfill routine requirements and normal warehouse stock replenishment.

Missed TATs shall continue to be worked ahead of other assigned

work within the same priority level. If the contractor fails to

complete an item within its designated TAT, the contractor shall

grant a credit to the Government for days late in excess of the

specified TAT.  See Credit paragraph 5.2.3.2.

No blanket exemptions will be given for items exceeding their

specified turn-around times due to an awaiting parts status or

awaiting repair by a subcontractor. The COTR will review and

consider valid delays on a case-by-case basis. Excusable delays, as

defined in the Default Clause, should be presented in writing to

the COTR, with a copy to the CO.

#### 5.2.3.1  Delinquent Priorities

The Contractor shall notify the COTR when any high priority (P1 – P4) workload item cannot be completed within its required TAT as listed in paragraph 5.2.3.

#### Credit

The amount of creditable late days shall be applied individually to each separate work order exceeding its specified TAT.  The amount of credit for each day in excess of the specified turn-around time shall be calculated based on the calibration or repair price as follows:

P1-SS/P1 - calculated at a 20% credit per late day, up to a maximum of 1 day or 20% credit.

P2 - calculated at a 10% credit per late day, up to a maximum of 2 days or 20% credit.

P3 - calculated at a 5% credit per late day, up to a maximum of 4 days or 20% credit.

P4 - the credit applied shall be based on the specified due date of the work order.  When the due date falls within the range of other listed priority time frames, the specified credit percentage shall apply.  For example: if a P4 has a due date which requires the work order to be accomplished within 8 calendar days, the credit to be applied if the TAT is not met would fall within the time frame for a P3.

P5 - calculated at a 4% credit per day, up to a maximum of 5 late days or 20% credit.

#### 5.2.3.3 Program Warranties

The contractor shall ensure quality in the services performed by providing warranties for specified programs listed below:

a. IP, EQ, FE,SS,CSA:

The contractor shall provide a 30-calendar day warranty period from completion date to cover the calibration only. This period of time allows for users to fully operate and utilize subject equipment to determine functionality of all internal circuitry.

b. IE,RR,SP:

The contractor shall provide a 60-calendar day warranty period from completion date.  This period of time allows for packing and shipping times and for field users to fully operate and utilize subject equipment to determine functionality of all internal circuitry.

c. ER:

The contractor shall provide a 90-calendar day warranty period from completion date. This period of time allows for warehouse storage, packing and shipping times, and for field users to fully operate 	and utilize subject equipment to determine functionality of all internal circuitry.

### 5.2.4 Workload Item Completion

The Contractor shall deliver completed workload items to a distribution point designated by the COTR.  The contractor shall provide copy 1 of the Production Order, AC Form 6000-11, computer generated production order, or shipping document to COTR for signature and subsequent return to the contractor. The contractor shall affix the pink “Requires Calibration – Do Not Use After” sticker to all ER completed items with a date of ninety days from completion date. This sticker ensures that no item shipped from serviceable stock will have less than nine months of calibration certification remaining. In the event an item being shipped exceeds the pink sticker date, the item is returned to the shop on an “SS” work order for re-calibration prior to shipment. See TE-11 for example forms/labels.

### 5.2.5 Calibration and Repair Criteria

#### 5.2.5.1 Calibration and Certification

The contractor shall perform all required calibrations and certifications within the guidelines of ANSI/NCSL Z540-1-1994, and job order documents provided by the Production Controller or COTR.

##### 5.2.5.1.1 Primary Standards

The contractor shall have all primary standards calibrated and certified by a higher echelon laboratory such as the National Institute of Standards and Technology (NIST).  The contractor shall be responsible for all costs including handling, transportation, and fees.  These standards shall be certified at or before the accepted minimum intervals specified by original manufacturer. (See TE-6).

##### 5.2.5.1.2 Working Standards

The contractor shall calibrate and certify all working standards under the guidelines of FAA Order 6200.4F. (See TE-6).

##### 5.2.5.1.3 Calibration Certificates

The contractor shall retain calibration certificates showing NIST traceability on all standards in accordance with FAA Order 6200.4F.

##### 5.2.5.1.4 Environmental Control

The contractor shall monitor and maintain records of environmental conditions within the PMEL in accordance with ANSI/NCSL Z540-1-1994.

#### 5.2.5.2 Repair

The contractor shall inspect, troubleshoot, clean, repair and replace individual components of assemblies and subassemblies, including CCAs.  The contractor shall repair/replace, as normal depot level maintenance, broken handles, bent frames, cracked cases, broken switches, damaged front and rear panels, defective/dirty filters, power cables, and replace miscellaneous missing/ defective parts, etc. The contractor shall be responsible for the purchase of all broken, defective and missing parts with the following exception. Missing ancillary cables, cases, covers, handles, plug-in units, or any missing item that would constitute an incomplete unit and/or having a value exceeding $50.00 will be replaced at government expense.  The contractor shall notify the COTR immediately upon discovery of received equipment in this category. Each item shall be calibrated and certified in accordance with FAA Order 6200.4F after completion of all repairs and modifications.

##### 5.2.5.2.1 Replacement Parts/Components

The contractor shall use exact replacement parts/components as specified by the workload item manufacturer.  Replacement parts/components having equal or better tolerances and parameters or used parts may be used only on an exception basis with written approval of the COTR. The contractor shall maintain a database of all replaced parts to include approved substitute and/or used parts by equipment type/model number. The substitute/used parts shall be separately identified in the database.

##### 5.2.5.2.2 Certification Labels and Stickers

The FAA will provide all equipment labels having an FAA/FAALC identification, i.e. FAALC certification and limited calibration, certification, cal void stickers and NCR labels.  The contractor shall provide and/or replace all other equipment labels/stickers. These stickers/labels shall include any manufacturers’ warning labels/stickers, which are required as a safety or operational warning notice. In the event a warning label sticker is missing or no longer legible it is the contractor’s responsibility to replace the sticker.

##### Beyond Economical Repair/Survey and RTO

The contractor shall advise the COTR when a workload item or GFE is considered to be beyond economical repair in order to be processed for survey or RTO. A workload item shall be considered beyond economical repair when parts are no longer available or if the cost of required parts and materials exceeds 75% of the unit cost as specified on the work order document. Unit cost is based on the AWC (average weighted cost) in LIS (Logistics Inventory System) or other government sources. All reasonable attempts shall be made to locate parts.  The contractor will be given access to Government supply databases for researching availability of parts when commercial sources are depleted. When parts are available through Government sources, the contractor shall inform the COTR in order to requisition the part(s). The contractor shall reimburse the Government for all parts procured through government sources to include shipping charges.  The contractor shall provide the COTR with a list of required parts, vendor’s prices, and vendor phone number attached to the “Beyond Economical Repair” document for confirmation purposes. The end item shall be considered beyond economical repair based upon the COTR’s findings. RTO items shall have a list of parts that can no longer be obtained attached to the unit for return to the customer. See example Survey document in TE-11.

##### 5.2.5.2.4 Cannibalization

Cannibalization of surveyed assets may be authorized by the COTR in order to obtain functioning part(s) no longer available from the manufacturer or other authorized sources.

#### 5.2.5.3 Modifications

The contractor shall perform FAA directed equipment modifications on workload items when directed by the COTR.  The Government will provide modification kits over $100.00.  All other modification kits/parts replacement kits intended for equipment repair or upgrade, which are deemed necessary by the manufacturer for repair are the sole responsibility of the contractor.

#### 5.2.5.4 Calibration Recall System

At start of base year period, the Government will provide Metrak Software for tracking FAALC in-use, IP Program test equipment and contractor assigned shop standards requiring calibration/ certification iaw FAA Order 6200.4F.  The contractor shall provide a monthly Metrak generated calibration due/overdue listing by work center to the COTR. The Government will provide updates (additions, deletions, and changes) as they occur.  The contractor shall, upon completion or termination of the contract, ensure the Metrak System is current prior to turn over to the Government or subsequent contractor.

#### 5.2.5.5 Cleaning

The contractor shall clean all workload items to remove dirt, dust, marks, rust, sticky residue, etc. utilizing appropriate commercial off the shelf cleaners.

### 5.2.6 Other Tasks

#### 5.2.6.1 Technical References

The contractor shall maintain a file of current references consisting of Performance Data Records (PDRs), technical/service manuals, modification records and safety notices in accordance with paragraph 5.1.3.(see TE-7)

#### 5.2.6.2 Contractor Developed Procedures

The contractor shall develop manual and automated test procedures as required, and submit all technical data and software to the COTR for approval before use.  All contractor-developed procedures shall become the property of the Government and all rights thereof, at contract expiration.

#### 5.2.6.3 Workload Item Receiving

The contractor shall unload, uncrate and unpack workload items and store all serviceable shipping containers in a location designated by the COTR.  The contractor shall use all serviceable shipping containers when available for repackaging completed workload items.

#### 5.2.6.4 Ancillary Equipment

The contractor shall advise the COTR in the event workload items are received without necessary ancillary equipment which would preclude the contractor from performing the assigned task.  The contractor shall not take further action on these workload items until the ancillary equipment is received or disposition instructions are received from the COTR.

#### 5.2.6.5 Manufacturers Warranties

The contractor shall be responsible for returning to manufacturers all equipment requiring repair under manufacturers warranty.  The contractor shall be responsible for all transportation fees.  Warranted items may be assigned to any workload program identified in paragraph 5.2.2.  The contractor shall be reimbursed under CLIN 11 for transportation fees incurred.

#### 5.2.6.6 Workload Subcontracting

The contractor shall be responsible for the maintenance and repair of all test equipment assets assigned to the contractor.  In the event an item assigned is beyond the capability of the contractor due to its proprietary nature or lack of specific standard, the contractor shall be responsible for returning the item to the manufacturer or certified lab having the capability to perform repair as appropriate.  The contractor shall be reimbursed at actual cost plus a nominal handling fee.  All warranties described in paragraph 5.2.3.3 shall apply. The contractor shall ensure that all subcontracted work is warranted and shall perform all applicable quality verification inspections upon return to this facility. The government will reimburse the contractor under CLIN 11.

#### 5.2.6.7 Workload Item Control

During the transition period the contractor shall develop an internal tracking system for all workload items under contractor control.  The contractor shall maintain the tracking system throughout the life of the contract.

#### 5.2.6.8 Documentation

The contractor shall complete and attach all required documentation, labels, and seals to completed workload items. All forms, labels, seals, and documents are subject to change. See TE-11 for examples.

a.  The contractor shall, on completed workload items coded IP and IE  complete and/or attach all seals, informational/warning labels and forms.  (AC Form 4510-1 or AC Form 4510-2, AC Form 4510-3, Performance Data Record (PDR) as required, and AC Form 6000-11).

b. 	 The contractor shall, on completed workload items coded SS attach all seals, informational/ warning labels and forms as instructed by the COTR.

c.  The contractor shall on completed workload items coded ER

attach all seals, informational/ warning labels and forms.  (AC Form 4510-1, or AC Form 4510-2, AC Form 4510-3, PDR, AC Form 6000-11) and bar code labels ( a bar code label printer is provided to the contractor for affixing to all ER work load items).

d.  The contractor shall, on completed workload items coded R&R attach all seals, informational/warning labels and forms. (AC Form 6040-51, AC Form 4510-1 or AC Form 4510-2, AC Form 4510-3, PDR, AC Form 6000-11).

- The contractor shall, on completed workload items coded EQ,

FE, and SP attach all seals, informational/warning labels and

forms.  These programs may require AC Forms 4510-1, 4510-2,

and 4510-3 or PDR’s and other forms as identified by the COTR.

#### Disposition Of Failed Equipment Due Calibration

The contractor shall advise the Production Controller of any IP and SS program items received that fail calibration.  Under these circumstances, the Production Controller will convert the IP (CLIN A/calibration) task to an IE (CLIN B/Repair) task and the contractor shall be reimbursed for the repair action only.  The SS tasks will be returned to reparable ER stock and the contractor will receive an equitable hourly rate for time under CLIN 10A.

#### Condition Tags

The contractor shall attach the appropriate (red condemned part, green reparable, or yellow serviceable) condition tag on all items returned to the Government.  In addition, any incomplete items returned shall include a list of missing parts on the reverse side of the condition tag.  (See TE-11)

# C-6  APPLICABLE DOCUMENTS

The Government will furnish, or make available for use, all FAA/AC Orders and Standards listed in TE-9.  Obtaining CFRs, NFPA, and ANSI standards shall be the responsibility of the Contractor.  All referenced Federal Laws, codes, directives and instructions in force at time of solicitation, unless coded otherwise shall be considered mandatory.  All other publications, documents, etc. reflected in TE-9 are applicable as coded.

## 6.1  General

The contractor is obligated to follow and adhere to those documents coded mandatory. Supplements or amendments to mandatory publications shall be considered to be in full force and effective upon receipt by the Contractor, except when such supplement or amendment is deemed to cause a change in cost of contract performance.  In such event, the contractor shall inform the CO, in writing, prior to implementation of such supplement or change.

## 6.2  Mandatory Directives

Mandatory directives are considered those regulations that are required to perform the required PWS services under normal situations.  The directives are mandatory in their entirety unless otherwise specified in Sections C-1 and C-5.  The Government will provide notification of all supplements, revisions or amendments to mandatory directives as they occur or are needed.  The Contractor shall maintain up-to-date files of mandatory directives.

### 6.2.1  Directive Revisions

All revisions to mandatory directives, as determined jointly by the CO and the Contractor, shall be implemented within five (5) working days of the Contractor's receipt of the revision.

## Required Forms

The Government will provide the forms listed in TE-11 that are required for the performance of this PWS.  The use of these forms is required unless the COTR determines that they may be disposed of or altered.  The Contractor is required to notify the COTR for replenishment of forms.