La-140

Reviewed by T. Nakagawa, JAERI, January 2004

1. Files

ENDF/B-VI:	The data were evaluated by Schenter and Schmitroth in 1974.

JENDL-3.3 and JENDL-3.2:

No data are given..

JEFF-3.0 and JEF-2.2:

ENDF/B-V was adopted for JEF-2. Charged particle emission cross sections (MT’s = from 104 to 111) were adopted from REAC-ECN-4. JEFF-3.0 is the same as JEF-2.2

CENDL-3:	No data are given.

BROND-2:	No data are given.

2. Thermal and resonance region

ENDF/B-VI

No resolved resonance parameters were given.

In the energy range below 61.274 eV, the capture cross section was assumed to be in the 1/v form with thermal cross section of 2.7 barns [Mu73] and the elastic scattering cross section to be a constant.

No unresolved resonance parameters are given.

JEFF-3.0 and JEF-2.2

The same as ENDF/B-VI.

Recommendation/conclusion for the thermal and resonance region

ENDF/B-VI is recommended.

3. Fast neutron region

(1) Methodology

ENDF/B-VI

Theoretical calculation was performed using the optical potential of Moldauer and statistical model. No threshold reaction cross sections were taken into account.

All angular distributions were assumed to be isotropic. Evaporation spectra were given to the continuum inelastic scattering.

JEFF-3.0 and JEF-2.2

The data of ENDF/B-VI were adopted for the total, inelastic and capture cross sections. The charged particle emission cross sections (MT=104 to 111) were adopted from REAC-ECN-4.

(2) Total cross section (MT=1)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La140.htm#mt1

(3) Capture cross section (MT=102)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La140.htm#mt102

(4) Elastic scattering cross section (MT=2)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La140.htm#mt2

(5) Inelastic scattering cross section (MT=4, 51 – 91)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La140.htm#mt4

Discrete levels considered in the evaluations are as follows:

ENDF/B-VI, JEFF-3.0	6 levels up to 0.581 MeV

The direct inelastic was not considered.

(6) (n,2n) reaction cross section (MT=16)

No data exist in the current evaluated data files.

(7) (n,p) reaction cross section (MT=103)

No data exist in the current evaluated data files.

(8) (n,) reaction cross section (MT=107)

See Fig: http://www.nndc.bnl.gov/sg21/fp21/htm/La140.htm#mt107

(9) Other reactions

The following reaction cross sections are given:

JEFF-3.0	(n,d), (n,t), (n,3He), (n,2p)

Recommendation/conclusion for the fast energy region

JEFF-3.0 (=JEF-2.2) is recommended.

References

[Ka49]	Katcoff S. et al.: J. Chem. Phys., 17, 421 (1949).

[Mu73]	Mughabghab S.F. and Garber D.I.: “Neutron Cross Sections, Vol. I,” BNL-325 3-rd Edition (1973).

[Mu81]	Mughabghab S.F. et al.: Neutron Cross Sections, Vol. 1, part A, Academic press (1981).

[Ob67]	O’brien H.A. et al.: J. Inorg. Nucl. Chem., 29, 584 (1967).

Table 1  Summary for Resolved and Unresolved Resonance Region: La-140

-----------------------------------------------------------------------------------------------------------------

Library	RRP	URP	Remarks

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI	not given 	not given	1/v region up to 61.274 eV

JEFF-3.0	not given 	not given	the same as ENDF/B-VI

-----------------------------------------------------------------------------------------------------------------

Table 2. Thermal Cross Sections and Resonance Integral: La-140

Units: barns

-----------------------------------------------------------------------------------------------------------------

Library/Experiment	Total	Elastic	Capture	Res.Integ.

-----------------------------------------------------------------------------------------------------------------

ENDF/B-VI	7.630	4.930	2.700	65.1

JEFF-3.0	7.630	4.930	2.700	65.1

Mughabghab et al. [Mu73]			2.7(0.3

Mughabghab et al. [Mu81]			2.7(0.3	69(4

Katcoff et al. [Ka49]			3.1(1.0*

O’brien et al. [Ob67]			2.7(0.3	69(4 (0.54 eV)

-----------------------------------------------------------------------------------------------------------------

*) Maxwell average.