| Company Name: | Equipment/Job Identification: Portable Crusher Move Type of Equipment: Crushers Make: CEC (Primary) Cedar Rapids (Secondary) Model: Year: Use: |
| --- | --- |
| Mine Name: |  |
| Date of Analysis: |  |

# Pre-Assessment

### List pre-requisites here

- New/Experienced Miner Training

- Site-specific Hazard Awareness Training

- Fall Protection Training (video, PPE, etc.)

- Location of safety equipment, etc.

- Rigging

- FEL Safety (videos)

# Duty 1: Tear Down (Cedar Rapids Cone Crusher)

Learner will demonstrate how to tear down the Cedar Rapids 124 Cone Crusher including all the steps listed below.  The learner will also explain job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  A thorough tear down procedure includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Empty crusher |  |  |  |  |
| De-energize power | Could cause personal injury due to accidental start-up, or electrocution |  |  |  |
| Lower stacking conveyor |  |  |  |  |
| Clean off catwalks |  |  |  | Be aware of people on ground |
| Take down spray bar |  |  |  |  |
| Block cone | Could damage cone bearings |  |  |  |
| Put stays on screen |  |  |  |  |
| Remove top two skirt boards |  |  |  |  |
| Remove tie-off cables |  |  |  | This is a new step at this time Use fall protection 10 foot ladder |
| Unhook the power cords | Could damage power cords |  |  |  |
| Wrap the cords up and bind | Could damage power cords |  |  |  |
| Clean out from under the crusher |  |  |  |  |
| Hook up the loader to the power pack | Could get pinched between loader and crusher Battery could explode |  |  | Discuss PPE, hook positive first, then negative |
| Raise the crusher to remove the screw jacks |  |  |  | Using power pack |
| Remove the screw jacks |  |  |  | Keep hands off top of jacks (pinch-point) |
| Fold up the front legs |  |  |  | Proper lifting procedures, positioning |
| Remove blocking and steel pads |  |  |  |  |
| Spot truck under crusher |  |  |  |  |

# Duty 2:  Mobilization (Cedar Rapids Cone Crusher)

Learner will demonstrate how to mobilize the Cedar Rapids 124 Cone Crusher.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Install oversize banner and two flags on tractor |  |  |  |  |
| Hook tractor to jeep |  |  |  | Ensure 5th wheel is locked properly |
| Check tires and hubs on jeep |  |  |  |  |
| Get crushing supervisor’s approval to hook up |  |  |  |  |
| Clean glad hands and king pin | Will not lock with dirty king pin |  |  | Clean with rag HazCom Training |
| Hook tractor and jeep up |  |  |  |  |
| Untape glad hands | Could result in brake failure |  |  |  |
| Hook up air lines and electrical cord | Could result in brake failure |  |  |  |
| Check tires and hubs on crusher |  |  |  |  |
| Pull unit to safe area after supervisor approval |  |  |  |  |
| Check all lights and brake performance |  |  |  | Be sure brakes work |
| Clean unit for loose stones, etc. |  |  |  |  |
| Install line bumpers |  |  |  |  |
| Install banner and flags |  |  |  | One oversize banner on rear, two flags on front, two flags in middle, two flags in the rear |
| Install strobe light on right rear side |  |  |  |  |
| Have crushing supervisor inspect unit one more time | Supervisor has ultimate responsibility for the move |  |  |  |
| Line up escort train |  |  |  |  |
| Proceed to new site Do not exceed 40 mph Maintain proper distance Check for overhead clearance | Could cause an accident, equipment damage, private property damage |  |  | Driver must know crusher actual height, width and route. Driver should know that 40 mph provides adequate breaking distance and minimizes damage from debris. |
| Arrive at new site Check with supervisor Park per instructions De-flag unit |  |  |  |  |

# Duty 3: Tear Down (Primary Crusher Unit)

Learner will demonstrate how to tear down the Primary Crusher Unit 110.  The learner will explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down procedures includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| De-energize power | Could cause personal injury due to accidental start-up, or electrocution |  |  |  |
| Unhook the power cords | Damage to cords |  |  |  |
| Take handrails down |  |  |  |  |
| Take ramps out with Loader |  |  |  |  |
| Clean primary |  |  |  |  |
| Put the stays on |  |  |  |  |
| Drop the electrical box down |  |  |  |  |
| Rollup the cords and place on top of electrical panel/box | Damage of cords could result |  |  |  |
| Secure with strap | Damage of cords could result |  |  |  |
| Put panel up on crusher with loader | Damage the panel/personal injury |  |  | Remain free of suspended loads |
| Hook loader to power pack | Potential pinch point/battery could explode |  |  | PPE, pinch point between the loader and primary, Hook positive up first. |
| Raise crusher |  |  |  | With power pack |
| Take out blocks and plywood and put in feeder (use loader) |  |  |  |  |
| Ready for truck |  |  |  |  |

# Duty 4:  Mobilization (Primary Crusher Unit)

Learner will demonstrate how to mobilize the Primary Crusher Unit 110.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Get approval from crushing supervisor to hook up primary |  |  |  |  |
| Clean king pin | Potential uncoupling |  |  | Hazard-Com awareness |
| Couple tractor to primary | Potential uncoupling |  |  | Double check fifth wheel lock |
| Un-tape glad hands | Potential brake failure |  |  |  |
| Hook up air and electric lines | Potential brake failure |  |  |  |
| Raise landing gear |  |  |  |  |
| Unhook power pack |  |  |  | Disconnect negative first |
| Move crusher to safe area to be cleaned |  |  |  | Get supervisory approval |
| Check all lights and brakes for performance | Potential brake failure |  |  |  |
| Check tires and hubs |  |  |  |  |
| Flag crusher |  |  |  | Two on tractor, one on each side of crusher, two on rear of crusher |
| Have supervisor inspect unit one more time |  |  |  |  |
| Proceed to new site Do not exceed 50 mph Maintain proper distance Check overhead clearances | Could cause an accident, equipment damage, private property damage |  |  | Driver must know crusher actual height, width and route. Driver should know that 50 mph provides adequate breaking distance and minimizes damage from debris. |
| Spot primary at new site |  |  |  | Get supervisors directions |
| De-flag |  |  |  |  |

# Duty 5:  Tear Down (Stacker Unit)

Learner will demonstrate how to tear down the Stacker Unit 126.  The learner will also explain job steps duties, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| De-energize power | Electrocution/accidental start-up |  |  |  |
| Wind up the cords | Damage to cords |  |  |  |
| Chain up counter weight |  |  |  | Before loosening belt |
| Loosen belt | Could damage belt |  |  |  |
| Lift up one wheel at a time | Potential pinch point hazard |  |  | Be sure to check rigging |
| Take drive chain off and hang and secure to frame |  |  |  |  |
| Pull pin | Potential pinch point hazard |  |  | Be aware of bucket hazards |
| Swing wheel into travel position | Potential pinch point hazard |  |  | Be aware of bucket hazards |
| Re-pin | Potential pinch point hazard |  |  | Be aware of bucket hazards |
| Shovel off pivot plate |  |  |  |  |
| Slide hopper to travel position |  |  |  |  |
| Hook to loader and raise up to proper height |  |  |  | Check rigging Stay clear of suspended loads |
| Clean fifth wheel plate and pin with shovel | Potential pinch-point/crushing hazard Potential uncoupling hazard |  |  | Stay clear of suspended loads |
| Put on truck with loader |  |  |  | Double check 5th wheel latch |
| Driver follows loader operator instructions |  |  |  | As crushing crew folds conveyor |
| Install belt tie-downs |  |  |  | Use fall protection |
| Unbolt at first pivot point |  |  |  | Use fall protection |
| Fold conveyor with the loader | Could result in personal injury Potential pinch-points |  |  | Stay clear of suspended loads |
| Lock conveyor into position | Could swing into oncoming traffic |  |  |  |
| Unhook loader |  |  |  | Use fall protection |
| Position loader to other end of conveyor |  |  |  |  |
| Hook loader |  |  |  | Use fall protection |
| Unbolt second pivot point |  |  |  | Use fall protection |
| Fold conveyor with loader | Could result in personal injury Potential pinch-points |  |  | Stay clear of suspended loads |
| Lock into position | Could swing into oncoming traffic |  |  |  |
| Unhook loader |  |  |  |  |
| Chain belt down at front pivot |  |  |  | Use fall protection |
| Lower tie off into transport position with ladder |  |  |  |  |

# Duty 6:  Mobilization (Stacker Unit)

Learner will demonstrate how to mobilize the Stacker Unit 126. The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Clean any stones or rocks off stacker |  |  |  |  |
| Check hubs for oil | Would adversely affect handling |  |  |  |
| Look for loose lug nuts | Would adversely affect handling |  |  |  |
| Look for soft tires | Would adversely affect handling |  |  |  |
| Plug in electrical lines |  |  |  |  |
| Flagging |  |  |  | Install one flag left front; 2 flags middle, one each side; 2 flags rear; two flags front of tractor and “oversize” banner |
| Pull slow on rough roads (no suspension) | Could damage machine |  |  |  |
| Check and maintain height and width clearances | Damage to property and pedestrians |  |  |  |
| Pull stacker to new site | See above |  |  |  |
| Check with supervisor on site |  |  |  |  |
| Find level area to drop landing gear |  |  |  |  |
| Block wheels on stacker | Equipment could roll |  |  |  |
| Drop landing gear |  |  |  |  |
| De-flag |  |  |  |  |
| Unhook electrical lines |  |  |  |  |
| Uncouple tractor and pull away carefully |  |  |  |  |

# Duty 7:  Tear Down (Tool Trailer Unit)

Learner will demonstrate how to tear down Tool Trailer Unit 125.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Secure contents |  |  |  | Make sure things won’t spill |
| Put steps and hand rails inside trailer (both sides) |  |  |  |  |
| Shut doors and lock |  |  |  |  |
| Ready for the truck |  |  |  |  |
| Have supervisor OK before coupling |  |  |  |  |
| Couple tool trailer | Possible uncoupling |  |  | Insure 5th wheel is latched properly |
| Hook up air and electrical lines | Possible brake failure |  |  |  |
| Crank up landing gear |  |  |  |  |
| Back trailer with spotter enough to remove grounding plate | Possible damage to grounding cable |  |  |  |
| Hang ground plate in its hanger |  |  |  |  |

# Duty 8:  Mobilization (Tool Trailer Unit)

Learner will demonstrate how to mobilize the Tool Trailer Unit 125.  The learner will also be able to explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Pull trailer to safe area of pit |  |  |  |  |
| Check brakes, hubs, tires, and lights | Possible brake failure |  |  |  |
| Move to new site under standard posted speeds unless conditions dictate otherwise | Possible traffic hazard |  |  | Maintain proper spacing and standard driving practices, follow posted speed limits |
| Spot tool trailer per supervisors instructions, un hook lines drop landing gear and uncouple tractor |  |  |  | Ask supervisor about ground plate |

# Duty 9:  Tear Down (Scale conveyor Unit, 30”, 24” transfer conveyors)

Learner will demonstrate how to tear down the Scale conveyor Unit 132, the 30” (107 Unit), and the 24” (100 Unit) transfer conveyors.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls. The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| De-energize power | Electrocution/accidental start-up |  |  |  |
| Wind up power cords Place scale cord on tool trailer Place power cord on scale conveyor | Damage to cords |  |  | Secure with bungee cord |
| Lower if necessary |  |  |  |  |
| Install bolts in stationary braces and secure |  |  |  |  |
| Clean it off |  |  |  |  |
| Check tires, hubs and lug nuts | Possible equipment break down, lost time |  |  |  |
| Pick up with loader to raise legs | Exposure to pinch points |  |  | Caution around suspended loads |
| Attach to truck and hook up electrical cords |  |  |  | Double check pintle hitch |

# Duty 10:  Mobilization (Scale convey or transfer conveyors)

Learner will demonstrate how to mobilize the Scale Conveyor Unit 132, the 30” (Unit 107), and the 24” (Unit 100) transfer conveyors.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check lights |  |  |  |  |
| Check brakes (132 only) | Possible brake failure |  |  |  |
| Hook up safety chain | Prevents break away |  |  |  |
| Check pintle is locked | Possible uncoupling |  |  |  |
| Drive to site | Possible loss of control at higher speed |  |  | Be aware of different handling characteristics of different trucks. Minimum 1 ton truck |

# Duty 11:  Tear Down Water Trailer

Learner will demonstrate how to tear down the Water Trailer Unit 105.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| De-energize | Electrocution/accidental start-up |  |  |  |
| Wind up cord | Damage to cords |  |  |  |
| Unhook and wind up hoses from Cedar Rapids | Damage to hoses |  |  |  |
| Secure lock box |  |  |  |  |
| Unhook hose and drain tank |  |  |  |  |
| Hook to pickup connect safety chains Connect electrical | Possible loss of load |  |  | Double check pintle hitch |
| Check lights and tires |  |  |  |  |
| Move to next site |  |  |  |  |

# Duty 12:  Tear Down Test Trailer

Learner will demonstrate how to tear down the Test Trailer Unit 49.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Secure contents and put steps inside | All testing equipment needs to go inside the trailer |  |  |  |
| De-energize if necessary and wrap cord under tool trailer | Electrocution/accidental start-up |  |  |  |
| Raise legs in back |  |  |  |  |
| Hook to pickup connect safety chains Connect electrical | Possible loss of load |  |  | Double check pintle hitch |
| Lower jack |  |  |  |  |
| Check lights and tires |  |  |  |  |
| Ensure porta-john is secure |  |  |  |  |
| Move to next site |  |  |  |  |

# Duty 13:  Mobilization (Water Trailer and Test Trailer)

Learner will demonstrate how to mobilize the Water Trailer Unit 105 and the Test Trailer Unit 49.  The learner will also be able to explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Observe speed limits and road conditions | Possible traffic accidents on public road |  |  | Observe speed limits and road conditions |
| Check hubs, tires, fasteners, hitch, safety chains and lights | Possible uncoupling / break away |  |  |  |

# Duty 14:  Mobilization (Loader)

Learner will demonstrate how to mobilize the loader.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Find level area to break deck on lowboy that is clear of overhead obstructions | Possible contact with power lines |  |  | Look over site |
| Pull chains and get approval from supervisor to load loader and gin pole |  |  |  |  |
| Place gin pole on center of lowboy deck |  |  |  |  |
| Put loader on deck, lower bucket | Possible for unit to slide off deck |  |  | Center loader, if slick use anti slip material on deck |
| Hook deck back together |  |  |  |  |
| Chain down loader with a minimum of 5 load rated chains | Possible loss of loader, personal injury |  |  | After 15 minutes of travel stop and recheck chains |
| Tape exhaust pipe and remove antenna | Possible engine damage |  |  | Tape exhaust to prevent turbo spin |
| Close all window and latch all doors |  |  |  |  |
| Flag Vehicle |  |  |  | Attach “oversized” banner on rear of low boy, two flags in the middle at the widest point(the bucket) Attach “oversized” banner on front of the tractor with 2 flags Minimum clearance is 14.5’ |
| Travel to new site (45 mph max) | Possible traffic hazards |  |  | Drive defensively |
| Arrive at new site, find flat area with no overhead obstructions to split deck | Possible contact with power lines |  |  |  |
| Unchain, deflag, untape exhaust, install antenna |  |  |  |  |
| Unload loader | Possible falling hazard, loader slipping off low boy in slick conditions |  |  | Use caution while entering or exiting the loader while it is on low boy |
| Remove gin pole from deck (crushing crew) |  |  |  |  |
| Put deck back together, and pick up chains |  |  |  |  |

# Duty 15:  Tear Down (Developer Unit)

Learner will demonstrate how to tear down the Developer Unit 106.  The learner will also be able to explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Remove ramp with loader |  |  |  |  |
| Energize system by starting engine |  |  |  |  |
| Lower stacking conveyor into travel position |  |  |  |  |
| Turn engine off (leave key in on position) and open a valve to de-energize | Relieves the pressure on the hose |  |  |  |
| Disconnect hoses |  |  |  |  |
| Restart engine |  |  |  |  |
| Lower landing gear to raise machine |  |  |  |  |
| Fold up spill/side plate with loader and secure |  |  |  |  |
| Unpin and raise front legs |  |  |  |  |
| Pull machine ahead with loader |  |  |  |  |
| Clean machine |  |  |  |  |
| Lower truss until collection hopper sits on ground |  |  |  |  |
| Unpin screen angle and drop down |  |  |  |  |
| Unpin the screen |  |  |  |  |
| Take hopper off with loader and gin pole and secure on belt bottom side up | Danger of pinch points, falling materials |  |  | Use fall protection Do not guide with hands - use shovel or tag line |
| Lower truss the rest of the way and put screen into transport position and re-pin |  |  |  |  |
| Clean king pin and un-tape glad hands | Possible brake failure |  |  |  |
| Couple tractor and hook up air lines | Possible brake failure |  |  | Double check 5th wheel latch |
| Raise landing gear (crushing crew) |  |  |  |  |
| Shut off engine |  |  |  |  |
| Put key in lock box |  |  |  |  |
| Clean unit |  |  |  |  |

# Duty 16:  Mobilization (Developer Unit)

Learner will demonstrate how to mobilize the Developer Unit 106.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check brakes, tires, hubs | Possible brake failure, equipment damage |  |  |  |
| Flag unit |  |  |  | 2 flags on front of truck 2 flags on rear of unit (one on each side) |
| Install light bar and check for proper operation |  |  |  |  |
| Check once more for rocks |  |  |  |  |
| Travel to new site Do not exceed 45 mph | Avoid loss of control |  |  | Maintain proper following distance |
| De-flag and see supervisor for drop location |  |  |  |  |
| Start engine |  |  |  |  |
| Lower landing gear to suitable position |  |  |  |  |
| Remove light bar and air lines |  |  |  |  |
| Disconnect tractor |  |  |  |  |

# Duty 17:  Tear Down (Developer Stacker Unit )

Learner will demonstrate how to tear down the Developer Stacker Unit 103.  The learner will also be able to explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The tear down process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Store 2-inch hydraulic hose on top of belt |  |  |  |  |
| Pick up one side with loader, pull pin axle and slide axle in and turn wheel and re-pin |  |  |  |  |
| Repeat steps for other wheel |  |  |  |  |
| Loosen the belt |  |  |  |  |
| Locate 5th wheel plate and place next to end of conveyor |  |  |  |  |
| Hook to tail pulley eye and lift with gin pole on the loader until head pulley is close to ground | Avoid pinch-points, falling material hazards |  |  | Be aware of suspended loads |
| Un-bolt conveyor at hinge point |  |  |  |  |
| Fold conveyor into transport position and re-pin |  |  |  | Avoid pinch-points |
| Lower conveyor to convenient height and install 5th wheel plate and install bolts | Avoid pinch-points |  |  | Fingers subject to pinching between 5th wheel plate and frame |
| Clean unit |  |  |  |  |
| Raise end to truck appropriate 5th wheel height | Avoid pinch-points, falling equipment |  |  | Be aware of suspended loads |
| Clean king pin | Possible detaching of unit |  |  | Clean using shovel - do not clean by hand |
| Hook up to truck |  |  |  |  |

# Duty 18:  Mobilization (Developer Stacker Unit )

Learner will demonstrate how to mobilize the Developer Stacker Unit 103.  The learner will also be able to explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The mobilization process includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Flag unit |  |  |  | 2 flags on front of truck 2 flags on rear of unit |
| Install light bar and test |  |  |  |  |
| Check tires and hubs | Failure could result in traffic hazard |  |  |  |
| Travel to next site Do not exceed 50 mph | Avoid loss of control |  |  |  |
| Check with supervisor and get directions |  |  |  |  |
| Lower landing gear, install braces |  |  |  | Install braces while still hooked to truck |
| Remove light bar and flags |  |  |  |  |
| Block tires | Unit could roll if not blocked |  |  |  |
| Uncouple |  |  |  |  |

# Duty 19:  Site Preparation

Learner will demonstrate how to prepare the site for crusher setup.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  Preparing the site for setup includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Examine site and evaluate any hazards | Unseen hazards can be discovered |  |  | Site examination should be done before equipment arrival Person conducting exam should be trained in site-specific hazards |
| Correct hazards if possible | Prevent personal injury |  |  |  |
| Site specific hazard awareness training given | Prevent personal injury |  |  |  |
| Task train for set up activities | Prevent person injury |  |  | Required by Part 46 (training requirements) |
| Level and stabilize pad for primary crusher and cedar rapids crusher with FEL |  |  |  |  |

# Duty 20: Equipment Placement

Learner will explain how to place the equipment at the site.  The learner will explain the steps involved in placing the equipment, the importance of the sequence, any associated risk, and how to implement appropriate controls.  The equipment placement sequence includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Hook loader to power pack on primary | Battery could explode Avoid pinch-points |  |  | Hook negative up last Maintain communications with FEL operator |
| Raise primary crusher |  |  |  |  |
| Replace temporary blocks under jacks |  |  |  |  |
| Remove electrical and air lines |  |  |  |  |
| Disconnect tractor and pull away |  |  |  |  |
| Place Cedar Rapids Unit 124 |  |  |  |  |
| Hook loader up to power pack on Cedar Rapids Raise discharge/front conveyor out of way Lock raised conveyor with two chains provide | Battery could explode Avoid pinch-points |  |  | Hook negative up last Maintain communications with FEL operator |
| Bring jacks down to ground and lift up crusher |  |  |  |  |
| Unhook electrical and air lines |  |  |  |  |
| Pull tractor away |  |  |  |  |
| Set up tool trailer next to pad |  |  |  |  |
| Put down ground plate |  |  |  | While truck is hooked |
| Place landing gear on the ground on (tool trailer) |  |  |  |  |
| Disconnect electrical and air lines and pull truck away |  |  |  |  |
| Drive truck to stacker unit 126 |  |  |  |  |
| Raise tie off cables out of travel position | Possible falling hazard |  |  | Use ladder/tie off |
| Hook up to stacker unit 126 |  |  |  |  |
| Lift landing gear |  |  |  |  |
| Go to most level open area available |  |  |  |  |
| Park truck at 90 degree angle to stacker |  |  |  | Driver will remain in cab and follow loader operator instructions |
| Hook on to head pulley end of conveyor | Possible falling hazard |  |  | Tie off Use lifting eyes to lift conveyor |
| Unfold the stacker with the loader and gin pole and into position | Possible falling machine |  |  | Keep clear of suspended loads |
| Secure the upper section with bolts | Possible falling hazard |  |  | Use fall protection |
| Unhook loader and gin pole | Possible falling hazard |  |  | Use fall protection |
| Relocate loader and hook to other end of stacker | Possible falling hazard |  |  | Use fall protection |
| Remove lock pin |  |  |  |  |
| Unfold into position |  |  |  | Keep clear of suspended loads |
| Secure lower section with bolts | Possible falling hazard |  |  | Use fall protection |
| Raise conveyor weight off of tractor with loader | Possible falling equipment |  |  | Keep clear of suspended loads |
| Unhook tractor |  |  |  |  |
| Pull tractor away |  |  |  |  |
| Set conveyor on ground |  |  |  |  |
| Unhook gin pole |  |  |  |  |
| Begin Leveling process Primary crusher Hook up loader to power pack Throw all blocking and plywood on ground Set level on machine Set machine level using jacks and blocks Unhook power pack Go to cedar rapids unit 124 Cedar rapids Hook up loader to power pack Lower legs to blocking position Set up machine using jacks and pads Lower the front conveyor Unhook the loader from the power pack | Battery could explode Possible pinch points Possible explosion Possible explosion Possible explosion |  |  | Hook up positive first, negative last Ensure area is clear of all people Unhook negative first Hook up positive first, negative last Unhook negative first |
| Set scale conveyor unit 132 Using gin pole and loader, hook to tongue of unit 132 Pull it into place |  |  |  |  |
| Set stacker unit 126 Use gin pole and loader to hook onto lift eyes of unit 126 Pull it into place Unhook from stacker unit 126 |  |  |  |  |
| Go to primary crusher unit 110 Hook onto electrical box Lift off and set on ground Unhook | Danger of suspended load |  |  | Keep ground personnel from under load |
| Take gin pole off of loader |  |  |  |  |
| Go to stacker unit 126 Pick one side up and turn wheel to radial position Repeat for opposite side Put drive chain on | Possible pinch-point Possible pinch-point |  |  | Be aware of bucket hazards Be aware of bucket hazards |

# Duty 21: Electrical Setup

Learner will demonstrate how to setup the electrical system for site.  The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The electrical setup procedures include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Unwrap cords and plug into receptacle into tool trailer |  |  |  | Do not plug in cords with generator running “anything that is rolled up has to be unrolled” |
| Hang or place cords to prevent damage |  |  |  | Discuss electrical standards: Explain 56.12004 (cable protection) “anything that is rolled up has to be unrolled” |
| Perform continuity/ground resistance test | Possible shock hazards/electrocution |  |  | Discuss electrical standards: Explain 56.12028 (ground testing) Explain 56.12016 (lock-out/tag-out) |

# Duty 22: Final Setup

Learner will demonstrate how to perform the final setup activities for the job site. The learner will also explain job steps, why they are conducted, any associated risk, and how to implement appropriate controls.  The final site setup includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Primary Crusher Place handrails Remove stays Set plywood Build ramp with mid-axle height berms Tape glad hands | Fall Hazard |  |  | Remove stays prior to operation |
| Cedar Rapids Take blocks out of cone Remove stays off of screen Reattach tie-off cables Reattach spray bar Tape glad hands | Fall Hazard Fall Hazard |  |  | Remove stays and blocks prior to operation |
| Stacker Tighten stacker belt Remove chain on counter-weight Remove the belt stays Put hopper in place | Fall Hazard |  |  | Tie off |
| Scale Conveyor Calibrate scale |  |  |  |  |
| Set test trailer Unhitch from truck Place steps Lower stabilizers |  |  |  |  |
| Water trailer Fill water tank Unhitch Reattach water system |  |  |  |  |
| Check appropriate signage |  |  |  |  |