NSTX

FAILURE MODES AND EFFECTS ANALYSIS

(FMEA)

Prepared By:			________________  	C Neumeyer (NSTX Project Engineer)

Reviewed By:			________________	J Chrzanowski (WBS 1)

________________	R Wilson (WBS 2)

________________	T Stevenson  (NBI Project)

________________	L Dudek (WBS 3)

________________	R Kaita (WBS 4)

________________	S Ramakrishnan  (WBS 5)

________________	G Oliaro  (WBS 6)

________________	J Levine (Safety Engineer)

TABLE OF CONTENTS

PREFACE	5

SCOPE	5

SAFETY IMPLICATIONS	6

LIST OF ACRONYMS	8

WBS Element:	1.1 Plasma Facing Components	9

Component:	 Graphite & Carbon Fiber Composite Tiles	9

Component:	 Passive Plates	10

Component:	 Inboard & Outboard Divertors	11

Component:	 NBI Protective Plates	12

WBS Element:	1.2 Vacuum Vessel & Support Structures	14

Component:	 Vacuum Vessel	14

Component:	 Support Structures	15

WBS Element:	1.3 Magnets	17

Component:	 Outer PF Coils (WBS 1.3.1)	17

Component:	 Outer TF Coils (WBS 1.3.2)	19

Component:	 TF Inner Leg Bundle (WBS 1.3.3.1)	21

Component:	 OH Solenoid (WBS 1.3.3.2)	23

Component:	 Shaping Coils (PF1a & PF1b) (WBS 1.3.3.3)	26

Component:	 Center Stack Casing (WBS 1.3.3.4)	28

Component:	 Water Cooled Flexible Cable Leads	30

WBS Element:	2.1  High Harmonic Fast Wave (HHFW) Radio Frequency (RF) System	31

WBS Element:	2.2  Coaxial Helicity Injection (CHI ) System	34

WBS Element:	2.3 Electron Cyclotron Heating (ECH) System	36

WBS Element:	2.4   Neutral Beam Injection (NBI) System	38

Component:	 NBI Duct	39

Component:	 NBI Vacuum Vessel	41

Component:	 Beam Line Acceleration System	42

Component:	 Cryopumping System	44

Component:	 NBI PLC Local Controller	46

WBS Element:	3.1 Vacuum Pumping System	47

Component:	 Main Pumping Duct	47

Component:	 Turbomolecular Pumps  (TMP)	49

Component:	 Roughing Pump Skid	51

Component:	 Backing Pump Skid	52

Component:	 N2 Vent Valves	53

Component:	 Vacuum Pumping System Local I&C	54

Component:	 Residual Gas Analyzer (RGA)	55

WBS Element:	3.2 Cooling Water System	56

Component:	 Water Distribution in Test Cell	56

Component:	 Pumps & Automatic Valves	59

Component:	 Auxiliary Components	50

Component:	 Cooling Water Local I&C	61

WBS Element:	3.3 Bakeout System	62

WBS Element:	3.4 Gas Delivery System (GDS)	64

WBS Element:	3.5 Glow Discharge Cleaning (GDC) System	66

WBS Element:	4X Diagnostics	67

Component:	 Flux Loops	68

Component:	 Thermocouples	69

WBS Element:	5X Power Systems	70

Component:	 AC Power Systems (WBS 5.1)	70

Component:	 AC/DC Power Supply Converters	73

Component:	 Safety Disconnect Switches	76

Component:	 DC Current Transducers	80

Component:	 Rochester Instrument System (RIS) Fault Detector	81

Component:	 Analog Coil Protection (ACP)	82

Component:	 Ground Fault Detection	83

Component:	 Power Supply Real Time Controller	84

Component:	 Hardwired Control System	86

WBS Element:	6X Central I&C	87

Component:	 EPICS Process Control System	87

Component:	 MDS+ Data Acquisition System	88

Component:	 Safety  System	89

WBS Element:	Operations	92

# PREFACE

### SCOPE

This revision of the NSTX FMEA is intended to reflect the configuration of the NSTX device and facility prior to day 2 (summer 2000) plasma operations. The FMEAs of certain systems which will not be operated at the time of day 2 plasma are not detailed herein. The systems specifically included/excluded from day 2 plasma operations are as follows:

WBS 11: PFCs – no exclusions

WBS 12: Vacuum Vessel – no exclusions

WBS 13: Magnets – no exclusions

WBS 21: High Harmonic Fast Wave RF System: no exclusions

WBS 22: Coaxial Helicity Injection (CHI) - no exclusions

WBS 23: Electron Cyclotron Heating (ECH) - no exclusions

WBS 24: Neutral Beam Injection (NBI) – no exclusions

WBS 31: Vacuum Pumping System – no exclusions

WBS 32: Water Cooling Systems – no exclusions

WBS 33: Bakeout System – will be operated up to 150C using water only

WBS 34: Gas Delivery System – no exclusions

WBS 35: Glow Discharge Cleaning (GDC) - no exclusions

WBS 4X: Diagnostics – magnetic and thermocouple diagnostics are included; others are excluded (non-essential)

WBS 5X: Power Systems – no exclusions

WBS 6X: Central I&C – no exclusions

NSTX will utilize the auxiliary systems of D-site. The TFTR FSAR includes FMEAs for these systems, including effects of failures on the auxiliary systems themselves. For NSTX this document only addresses failures which impact the NSTX device. Effects of failures on the auxiliary systems themselves are covered by the TFTR FSAR.

In general, single failure modes are addressed. In some cases, for failures which would have severe consequences in terms of damage to hardware or risk to personnel safety, multiple failures are addressed.

### SAFETY IMPLICATIONS

Certain failures can increase the risk of injury to personnel. For any particular failure, the level of risk of injury to personnel depends on several factors including:

1) the nature of the failure

2) the presence or absence of features which mitigate the effect of the failure (e.g. redundancy, energy isolating barriers, etc.)

3) the presence or absence of personnel in the area where the failure has occurred

4) the level of training of the personnel

This FMEA addresses 1) and 2) above. Items 3) and 4) relate mainly to administrative procedures which aim to prevent access to hazardous areas or to limit access to personnel trained to conduct themselves safely in potentially hazardous areas. This FMEA does not address administrative procedures.

This FMEA addresses new systems which will exist in the NSTX Test Cell, as well as other D-site systems whose failure could damage the NSTX device, or which have been significantly modified for use on NSTX, or which relate to safe access to the NSTX Test Cell.

This FMEA does not  address safety issues related to the conduct of operations throughout the balance of the D-site facility. Considering that the safety of operations of TFTR was documented and approved via the TFTR FSAR, and demonstrated to be effective for more than a decade,  it would not add to the safety of NSTX operations to repeat that analysis herein.

Considering its role in establishing safe access to the NSTX Test Cell, the Safety Lockout Device (SLD), along with the interface between the SLD and the power supply system Safety Disconnect Switches (SDS), and the supervision of operation of the power supply system by the Hardwired Interlock System (HIS), these safety related systems have been addressed herein, even though they have not been changed for NSTX in any substantial way.  The SLD and SDS interface remain absolutely unchanged. The HIS has been modified to reflect the simpler requirements for NSTX but the TFTR concepts (redundancy, etc.) and actual components have been fully retained.

Hot Access is a special mode which allows for the presence of a limited number of personnel in the NSTX Test Cell during coil energization in order that they can observe first hand any unexpected behavior. These persons will each have in their possession a key which locks the HIS in the Hot Access Mode, preventing simultaneous TF and PF energization (and the possibility of plasma formation) using exactly the TFTR HIS interlocking mechanism. Compared to an observer outside of the NSTX Test Cell, these persons will unavoidably be exposed to a higher level of risk of injury.  However, via design of protective shields as well as administrative procedures to ensure their use, all reasonable measures will be taken to minimize this risk. The design of these shields and the administrative procedures is outside of the scope of this FMEA. However, it is expected that the design of these shields will be similar to the design used for TFTR, and it is noted that the ability of NSTX to emit projectile is considerably less than TFTR, owing to its much lower magnetic fields.

#### RECOVERY FROM FAILURES

Associated with each failure is a recovery time and cost. Features of NSTX which serve to facilitate recovery are as follows:

-	sufficient spare OH coil conductor was purchased such that a new coil can be wound, if required, while avoiding the 3-4 month delay to obtain new custom extruded conductor

-	the NSTX PF coil design  has inherent modularity  (PF2, 3, 4, and 5 consist of “a” and “b” parts, either of which could be disconnected in case of failure, while energizing the remaining part)

-	the NSTX PF4 coil could serve as a back-up for PF5, in case of a failure of the latter, without a dramatic impact on the program (the “dimple” would be present in the plasma shape until such time that the failed coil was replaced)

-	a limited number (one quadrant) of TF inner legs were purchased such that the fabrication of a new TF inner leg bundle could begin while conductors for the remaining quadrants were being extruded, thereby reducing the recovery time

-	the design of the TF outer legs is such that, in case of failure, new conductors can be formed from standard bar stock with a slot milled in the edge.

-	spare parts for one ceramic insulator assembly are in possession; beyond this the options exist for removing assemblies from TFTR (e.g. pump or NBI ducts), or having entirely new assemblies fabricated

-	in general,  NSTX makes use of a subset of the TFTR equipment (e.g. power supplies) such that the remaining unused components can serve as spares or as sources of spare parts

# LIST OF ACRONYMS

| ACP | Analog Coil Protection system | NSTX | National Spherical Torus Experiment |
| --- | --- | --- | --- |
| B | magnetic field | NTC | NSTX Test Cell |
| CHI | Coaxial Helicity Injection | OH | Ohmic Heating |
| COE | Chief Operating Engineer | PAUX | Permissive relay for Auxiliary Systems |
| DCCT | DC Current Transducer | PC Link | Power Conversion (power supply command data ) Link |
| DCPT | DC Potential (voltage) Transducer | PF | Poloidal Field |
| E-stop | Emergency Stop | PFC | Plasma Facing Component |
| ECH | Electron Cyclotron Heating | PLC | Programmable Logic Controller |
| EIC | (FCPC) Engineer In Charge | PPPL | Princeton Plasma Physics Lab |
| EPICS | Experimental Physics Instrumentation & Control System | PSRTC | Power Supply Real Time Controller |
| FCPC | Field Coil Power Conversion | RF | Radio Frequency |
| FMEA | Failure Modes & Effects Analysis | RGA | Residual Gas Analyzer |
| HCS | Hardwired Control System (in FCPC) | RIS | Rochester Instrument System (fault detector) |
| HHFW | High Harmonic Fast Wave | rms | root mean square |
| HIS | Hardwired Interlock System | SDS | Safety Disconnect Switch |
| HSC | Halmar Signal Conditioner | SLD | Safety Lockout Device |
| HVAC | Heating/Ventilating/Air Conditioning | SOL | Scrape Off Layer |
| I | current | TF | Toroidal Field |
| I&C | Instrumentation & Control | TFTR | Tokamak Fusion Test Reactor |
| I/O | Input/Output | TMB | Trimethylboron |
| IR | Infra Red | TMP | Turbo Molecular Pump |
| LEC | Liquid Effluent Collection tank | UPS | Uninterruptable Power System |
| MGD | Master Gate Driver | VPS | Vacuum Pumping System |
| NBI | Neutral Beam Injection | WBS | Work Breakdown Structure |

# WBS Element:	1.1 Plasma Facing Components

## Component:		Graphite & Carbon Fiber Composite Tiles

Function:	The PFC (Inner Wall, Inboard Divertor, Outboard Divertor, and Passive Plate) Tiles comprise the surface which interacts with the plasma and forms the plasma boundary

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Tile overheating due to misalignment, or plasma misoperation (control system failure, CHI misoperation, etc.) | Impurity influx into plasma, reduced performance | Visible camera, Infra Red (IR) camera, Residual Gas Analyzer (RGA) | Control plasma shape and Scrape Off Layer (SOL) to avoid localized heating, repair tile when vacuum vessel accessible. |
| Partial (cracked tile) or complete tile detachment from mounting surface/backplate due to thermal shock and/or eddy currents and electromagnetic forces. | Loose tile piece will fall down in vacuum vessel, could bridge isolating gap (e.g. ceramic insulator, passive plate toroidal gap, etc.), leading to localized diversion of plasma. | Visible camera, IR camera (depending on effect). | Repair tile, remove broken piece(s) when vacuum vessel accessible. |
| Tile support rail or T-bar or other mounting hardware detachment from mounting surface/backplate due to thermal shock and/or eddy currents and electromagnetic forces. | Loose metallic piece will fall down in vacuum vessel, could bridge isolating gap (e.g. ceramic insulator, passive plate toroidal gap, etc.), leading to localized diversion of plasma. | Visible camera, IR camera (depending on effect). | Shutdown, vent vacuum vessel, repair |

# WBS Element:	1.1 Plasma Facing Components

## Component:		Passive Plates

Function:	The Passive Plates provide transient stabilization of the plasma vertical position, and determine the plasma outboard boundary.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loose connections leading to excessive contact electrical resistance on toroidal or poloidal segment-to-segment jumpers, or saddle jumpers | Electrical arcs, local copper melting, excessive resistance and reduction in current flow, impurity influx into plasma, reduced performance | Visible camera, Infra Red (IR) camera, Residual Gas Analyzer (RGA), magnetic diagnostics | Repair when vacuum vessel accessible |
| Loose connections leading to excessive contact thermal resistance on toroidal segment-to-segment jumpers. | Increased thermal resistance, higher plate temperatures during operations, lower plate temperatures during bakeout., higher thermal gradients, higher stresses, reduced performance | Thermocouples, IR camera. | Repair when vacuum vessel accessible |
| Mechanical deformation/failure of supports due to eddy currents and electromagnetic forces. | Misalignment and/or dislocation of plate structures into plasma envelope, loss of machine operability | Visible camera | Shutdown, vent vacuum vessel, repair |
| Cooling circuit leak | Release of heat exchanger fluid into vacuum vessel | Residual Gas Analyzer (RGA) | Shutdown, vent vacuum vessel, repair, bakeout |
| See PFC Tile FMEA |  |  |  |

# WBS Element:	1.1 Plasma Facing Components

## Component:		Inboard & Outboard Divertors

Function:	The Inboard & Outboard Divertors provide Scrape Off Layer (SOL) heat flux and impurity targets for diverted (X-point) plasmas. The Lower Inboard & Outboard Divertors provide the sink and source for the CHI current drive.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Outboard Divertor, Loose connections leading to excessive contact electrical resistance on plate-to-ring connections. | Electrical arcs, local copper melting, impurity influx into plasma, reduced performance | Visible camera, Infra Red (IR) camera, Residual Gas Analyzer (RGA), magnetic diagnostics | Repair when vacuum vessel accessible |
| Outboard Divertor, Mechanical deformation/failure of supports due to eddy currents and electromagnetic forces. | Misalignment and/or dislocation of plate structures into plasma envelope, loss of machine operability | Visible camera | Shutdown, vent vacuum vessel, repair |
| Outboard Divertor, Cooling circuit leak | Release of heat exchanger fluid into vacuum vessel | Residual Gas Analyzer (RGA) | Shutdown, vent vacuum vessel, repair, bakeout |
| See PFC Tile FMEA |  |  |  |

# WBS Element:	1.1 Plasma Facing Components

# Component: 	NBI Protective Plates

Function:	The Protective Plates consist of an array of graphite tiles mounted on a structure inside the NSTX vacuum vessel centered about the midplane at bays H & I. The system is designed  to absorb neutral beam energy that is not absorbed by the plasma.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Tile overheating due to misalignment or non-conventional beam strike | Impurity influx into plasma, reduced performance | Visible camera, Infra Red (IR) camera, Residual Gas Analyzer (RGA) & Thermal couples | Terminate beam operation. |
| Partial (cracked tile) or complete tile detachment from mounting surface/backplate due to thermal shock and/or eddy currents and electromagnetic forces. | Loose tile piece will fall down in vacuum vessel, could bridge isolating gap (e.g. ceramic insulator, passive plate toroidal gap, etc.), leading to localized diversion of plasma. | Visible camera, IR camera (depending on effect). | Vent machine & Repair tile, remove broken piece(s) when vacuum vessel accessible. Consider limitation of beam operation. |
| Tile support rail or T-bar or other mounting hardware detachment from mounting surface/backplate due to thermal shock and/or eddy currents and electromagnetic forces. | Loose metallic piece will fall down in vacuum vessel, could bridge isolating gap (e.g. ceramic insulator, passive plate toroidal gap, etc.), leading to localized diversion of plasma. | Visible camera, IR camera (depending on effect). | Shutdown, vent vacuum vessel, repair |
| Loose support connections leading to excessive contact electrical resistance | Electrical arcs, local copper melting, excessive resistance and reduction in current flow, impurity influx into plasma, reduced performance | Visible camera, Infra Red (IR) camera, Residual Gas Analyzer (RGA), | Repair when vacuum vessel accessible |

# WBS Element:	1.1 Plasma Facing Components			Component: 	NBI Protective Plates (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loose tile connections leading to poor thermal contact. | Increased thermal resistance, higher plate temperatures during operations, lower plate temperatures during bakeout., higher thermal gradients, higher stresses, reduced performance | Thermocouples, IR camera & thermal couples | Repair when vacuum vessel accessible |
| Mechanical deformation/failure of supports due to eddy currents and electromagnetic forces. | Misalignment and/or dislocation of plate structures into plasma envelope, loss of machine operability | Visible camera | Shutdown, vent vacuum vessel, repair |
| Cooling circuit leak | Release of heat exchanger fluid into vacuum vessel | Residual Gas Analyzer (RGA) | Shutdown, vent vacuum vessel, repair, bakeout |

# WBS Element:	1.2 Vacuum Vessel & Support Structures

## Component:		Vacuum Vessel

Function:	The vacuum vessel provides the high vacuum environment for plasma operations.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Excessive deformation of structural materials | Misalignment of components (e.g. PFCs, RF antenna) mounted on vacuum vessel | Visible Camera, Infrared (IR) camera, magnetic diagnostics | Shutdown, vent vacuum vessel, repair |
| Failure of structural materials or welds | Leak | Residual Gas Analyzer (RGA), and Vacuum Pumping System pressure gauges | Shutdown, vent vacuum vessel, repair |
| Failure of port flange vacuum seal connections | “ | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |

# WBS Element:	1.2 Vacuum Vessel & Support Structures

## Component:		Support Structures

Function:	The coil support structures provide mechanical support for the outer PF coils and outer TF coil legs, and provide dielectric breaks where required (PF5). The vacuum vessel legs support the vacuum vessel and provide dielectric breaks.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Failure of coil support structural materials or welds due to electromagnetic, vacuum and/or thermal loads | Misalignment, movement, or dislocation of outer PF coils or outer TF coil legs, perturbation of magnetic field topology, possible mechanical damage to coil leading to coil electrical damage (ground fault or turn to turn fault). | Maintenance inspection, magnetic diagnostics, power supply system ground fault detector. | Shutdown, vent vacuum vessel, repair |
| Failure of sliding joint in outer PF coil supports (excessive resistance to sliding motion). | Misalignment and/or deformation of outer PF coils, perturbation of magnetic field topology, possible mechanical damage to coil leading to coil electrical damage (ground fault or turn to turn fault). | Maintenance inspection, magnetic diagnostics, power supply system ground fault detector. | Shutdown, vent vacuum vessel, repair |

WBS Element:	1.2 Vacuum Vessel & Support Structures	Component:		Support Structures	(con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Failure of sliding joint of umbrella structure (excessive resistance to sliding motion). | Excessive stress in umbrella and vacuum vessel during bakeout, possible structural deformations, failure of welds, weakening of structure | Maintenance inspection, magnetic diagnostics. | Shutdown and repair |
| Failure of sliding joint of vacuum vessel leg support (excessive resistance to sliding motion). | Excessive stress in leg and structure during bakeout, possible structural deformations, failure of welds, weakening of structure, possible dislocation of vacuum vessel, loss of vacuum integrity | Monitoring of displacement of vacuum vessel. Maintenance inspection. | Shutdown and repair |
| Failure of dielectric joint(s) associated with outer PF coils supports or vacuum vessel leg supports | During non-CHI operations, conducting electrical loops, perturbation of magnetic field. During CHI operations, fault on CHI power supply, arcing, burning, melting. | Maintenance inspection & test, magnetic diagnostics, power supply system ground and overcurrent fault detection. | Shutdown and repair |

# WBS Element:	1.3 Magnets

## Component:		Outer PF Coils (WBS 1.3.1)

Function:	The Outer PF Coils contribute the magnetic field topology required for plasma position and  shape control.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Blockage of cooling water circuit | Reduction in cooling water flow, reduction in rate of cooling between pulses. | Flow switches which are interlocked to prevent power supply operation | Shutdown and flush/clear coolant passage. |
| Leak in cooling water circuit | Depending on extent of leak, reduction in cooling water flow, possible ground fault | Flow switches, power supply system ground fault detection, visual inspection | Shutdown and repair. |
| Delamination/debonding of turn-to-turn insulation | Possible motion of conductors under load, abrasion, eventual electrical failure | None | None |
| Electrical failure of groundwall insulation at single location | If non-CHI operations, or CHI operations and outer vacuum vessel grounded, small leakage current to ground (limited by high resistance grounding), and redistribution of voltage to ground. If CHI operations and outer vacuum vessel energized by CHI power supply, small leakage current between CHI and affected PF circuit. | Power supply system ground fault detector. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets						Component:		Outer PF Coils (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Electrical failure of turn-to-turn insulation | Fault current flow in shorted turns, opposite to direction of normal current flow to oppose flux produced by non-shorted turns, large internal repulsive forces between shorted and non-shorted turns, arcing, burning, and melting in region of failure, possible destruction of coil. | Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace. |
| Loss of contact pressure leading to excess electrical contact resistance and /or open circuit condition under load at coil terminals or coil leads | Excess joint resistance and heating, arcing, melting, if lead(s) become physically disconnected, could be displaced from normal point of connection, possible diversion of current into other metallic path(s), possible destruction of coil. | Maintenance (bolt torque), inspection (temperature stickers), test (joint resistance measurement); Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets

## Component:		Outer TF Coils (WBS 1.3.2)

Function:	The Outer TF Coils provide the return path for the Inner Leg TF Bundle

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Blockage of cooling water circuit | Reduction in cooling water flow, reduction in rate of cooling between pulses. | Flow switches which are interlocked to prevent power supply operation | Shutdown and flush/clear coolant passage. |
| Leak in cooling water circuit | Depending on extent of leak, reduction in cooling water flow, possible ground fault | Flow switches, power supply system ground fault detection, visual inspection | Shutdown and repair. |
| Delamination/debonding of turn-to-turn insulation | Possible motion of conductors under load, abrasion, eventual electrical failure | None | None |
| Electrical failure of groundwall insulation | If non-CHI operations, or CHI operations and outer vacuum vessel grounded, small leakage current to ground (limited by high resistance grounding) and redistribution of voltage to ground. If CHI operations and outer vacuum vessel energized by CHI power supply, small leakage current between CHI and TF | Power supply system ground fault detector. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets						Component:		Outer TF Coils (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Electrical failure of turn-to-turn insulation | Fault current flow in shorted turns, opposite to direction of normal current flow to oppose flux produced by non-shorted turns, large internal repulsive forces between shorted and non-shorted turns, arcing, burning, and melting in region of failure, possible destruction of coil. | Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace. |
| Loss of contact pressure leading to excess electrical contact resistance and /or open circuit condition under load at coil terminals or coil leads | Excess joint resistance and heating, arcing, melting, if lead(s) become physically disconnected, could be displaced from normal point of connection, possible diversion of current into other metallic path(s), possible destruction of coil. | Maintenance (bolt torque), inspection (temperature stickers), test (joint resistance measurement); Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets

## Component:		TF Inner Leg Bundle (WBS 1.3.3.1)

Function:	The TF Inner Leg Bundle current forms the toroidal field for plasma confinement.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Blockage of cooling water circuit | Reduction in cooling water flow in blocked paths, differential temperature between turns in bundle, reduction in rate of cooling between pulses. | Flow switches which are interlocked to prevent power supply operation | Shutdown and flush/clear coolant passage |
| Leak in cooling water circuit | Depending on extent of leak, reduction in cooling water flow, possible ground fault | Flow switches, power supply system ground fault detection, visual inspection | Shutdown and repair |
| Delamination/debonding of turn-to-turn insulation | Possible motion of conductors under load, abrasion, eventual electrical failure | None | None |
| Electrical failure of groundwall insulation | Small leakage current to ground (limited by high resistance grounding), and redistribution of voltage to ground. | Power supply system ground fault detector | Shutdown, repair if possible, or replace |
| Electrical failure of turn-to-turn insulation | Fault current flow in shorted turns, opposing current flow and flux produced by non-shorted turns, large internal repulsive forces between shorted and non-shorted turns, arcing, burning, and melting in region of failure, possible destruction of coil | Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace |

WBS Element:	1.3 Magnets					Component:		TF Inner Leg Bundle (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of structural integrity of hub assembly and/or contact pressure on radial flags connecting inner legs to flexible connectors | Excess joint resistance and heating, possible contact surface melting, arcing, could lead to open circuit condition | Maintenance (bolt torque), inspection (temperature stickers), test (joint resistance measurement) | Shutdown and repair |
| Loss of contact pressure on flexible joints connecting radial flags to outer legs | Excess joint resistance and heating, possible contact surface melting, arcing, could lead to open circuit condition | Maintenance (bolt torque), inspection (temperature stickers), test (joint resistance measurement) | Shutdown and repair |

WBS Element:	1.3 Magnets

## Component:		OH Solenoid (WBS 1.3.3.2)

Function:	The OH Solenoid provides loop voltage for plasma initiation and flux swing for inductive generation of plasma current

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Blockage of cooling water circuit during normal operations, | Reduction in coolant flow and heat removal rate between pulses, reduced performance (reduced pulse repetition rate) | Flow switches which are interlocked to remove power supply permissive via PAUX relay | Monitor cooling water flows and temperatures, and OH coil groundwall temperatures, continue operations at reduced repetition rate or discontinue. Flush/clear coolant passage after shutdown. |
| Blockage of cooling water circuit during bakeout | Reduction in coolant flow and heat removal rate, interruption of bakeout or reduction in allowable bakeout temperature | Flow switches and thermocouples measuring temperature of water returning to outlet manifold, thermocouples measuring temperature of OH groundwall insulation. | Discontinue heat input and/or switch to cooling, monitor cooling water flows and temperatures, and OH coil groundwall temperatures, continue bakeout at reduced temperature or discontinue. Flush/clear coolant passage after bakeout shutdown. |
| Leak in cooling water circuit | Depending on extent of leak, reduction in cooling water flow, possible ground fault | Flow switches, power supply system ground fault detection, visual inspection | Shutdown and repair. |

WBS Element:	1.3 Magnets						Component:		OH Solenoid (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Delamination/debonding of turn-to-turn insulation | Possible motion of conductors under load, abrasion, eventual electrical failure | None | None |
| Electrical failure of groundwall insulation | Small leakage current to ground (limited by high resistance grounding), and redistribution of voltage to ground. | Power supply system ground fault detector. | Shutdown, repair if possible, or replace. |
| Electrical failure of turn-to-turn insulation | Fault current flow in shorted turns, opposite to direction of normal current flow to oppose flux produced by non-shorted turns, large internal repulsive forces between shorted and non-shorted turns, arcing, burning, and melting in region of failure, possible destruction of coil. | Magnetic diagnostics. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets						Component:		OH Solenoid (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Mechanical failure of in-line conductor or conductor joint | High resistance, overheating, arcs, burning, melting | Excessive coil impedance | Shutdown, remove center stack and OH coil, repair if possible, or replace |
| Loss of contact pressure leading to excess electrical contact resistance and /or open circuit condition under load at coil terminals or coil leads | Excess joint resistance and heating, arcing, melting, if lead(s) become physically disconnected, could be displaced from normal point of connection, possible diversion of current into other metallic path(s), possible destruction of coil. | Maintenance (bolt torque), inspection (temperature stickers), test (joint resistance measurement); Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets

## Component:		Shaping Coils (PF1a & PF1b) (WBS 1.3.3.3)

Function:	PF1a provides plasma shaping. PF1b provides control of the shape of the X-point for CHI and provides a means for plasma current Rogowski Loop calibration.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Blockage of cooling water circuit | Reduction in cooling water flow, reduction in rate of cooling between pulses. | Flow switches which are interlocked to prevent power supply operation | Shutdown and flush/clear coolant passage. |
| Leak in cooling water circuit | Depending on extent of leak, reduction in cooling water flow, possible ground fault | Flow switches, power supply system ground fault detection, visual inspection | Shutdown and repair. |
| Delamination/debonding of turn-to-turn insulation | Possible motion of conductors under load, abrasion, eventual electrical failure | None | None |
| Electrical failure of groundwall insulation | Small leakage current to ground (limited by high resistance grounding), and redistribution of voltage to ground. | Power supply system ground fault detector. | Shutdown, repair if possible, or replace. |
| Electrical failure of turn-to-turn insulation | Fault current flow in shorted turns, opposite to direction of normal current flow to oppose flux produced by non-shorted turns, large internal repulsive forces between shorted and non-shorted turns, arcing, burning, and melting in region of failure, possible destruction of coil. | Magnetic diagnostics. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets				Component:		Shaping Coils (PF1a & PF1b) (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of contact pressure leading to excess electrical contact resistance and /or open circuit condition under load at coil terminals or coil leads | Excess joint resistance and heating, arcing, melting, if lead(s) become physically disconnected, could be displaced from normal point of connection, possible diversion of current into other metallic path(s), possible destruction of coil. | Maintenance (bolt torque), inspection (temperature stickers), test (joint resistance measurement); Magnetic diagnostics, unusual electrical impedance and response to power supply excitation. | Shutdown, repair if possible, or replace. |

WBS Element:	1.3 Magnets

## Component:		Center Stack Casing (WBS 1.3.3.4)

Function:	The Center Stack Casing provides the inner vacuum boundary, and is physically connected to the vacuum vessel but electrically isolated via ceramic insulator assemblies. The Inner Wall PFCs are attached to and supported by the Center Stack Casing. Thermal Insulation within the Center Stack Casing bore serves to thermally isolate the OH coil from the casing. Pedestal mounted to test cell floor provides support and dielectric breaks.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Excessive deformation of structural materials | Misalignment of PFC components. | Visible Camera, Infrared (IR) camera, magnetic diagnostics | Shutdown, vent vacuum vessel, repair |
| Failure of structural materials or welds | Leak | Residual Gas Analyzer (RGA), and Vacuum Pumping System pressure gauges | Shutdown, vent vacuum vessel, repair |
| Failure of vacuum seal connections | “ | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Electrical breakdown of ceramic insulator | During non-CHI operations, conducting electrical loops, perturbation of magnetic field. During CHI operations, fault on CHI power supply, arcing, burning, melting, possible loss of vacuum conditions | Power supply overcurrent and ground fault detection, Visible Camera, Infrared (IR) camera, magnetic diagnostics, Residual Gas Analyzer (RGA), and Vacuum Pumping System pressure gauges. | Shutdown, vent vacuum vessel, repair if possible or replace |

WBS Element:	1.3 Magnets					Component:		Center Stack Casing (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Electrical breakdown of thermal insulation | If during CHI operations with center stack casing energized, fault current flow through OH coil ground plane and instrumentation mounted thereon, arcing, burning, melting, possible OH ground fault and possible destruction of OH coil. | OH and CHI power systems ground fault detection systems. | Shutdown, remove center stack assembly and OH coil, repair if possible or replace. |
| Degradation of thermal insulation due abrasion, heat, or coolant leak from coil system etc. | Low thermal resistance between center stack casing and OH/PF1a, excess temperature rise on OH/PF1a coil ground plane, reduced performance (reduced repetition rate and bakeout temperature). | Thermocouples on OH and PF1a coil ground planes. | Shutdown, remove center stack assembly and repair |

WBS Element:	1.3 Magnets

## Component:		Water Cooled Flexible Cable Leads

Function:	The Water Cooled Flexible Cable Leads provide the electrical connection between the terminals of the WBS 5 air cooled bus and the magnet coil terminals.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Water leak | Water on floor, depending on extent of leak, possibly draining to Liquid Effluent Collection (LEC) tank, possible ground fault, small leakage current to ground limited by high impedance grounding resistors | Depending on extent of leak, flow switch drop out, ground fault indication on power supply system ground fault detector | Repair or replace |
| Electrical breakdown of dielectric | Likely to occur on one conductor first, accompanied by a water leak, possible ground fault, small leakage current to ground limited by high impedance grounding resistors, prior to developing unnoticed into a line-line fault | Water leak and/or electrical leakage to ground, depending on extent of water leak, possible flow switch drop out, possible ground fault indication on power supply system ground fault detector | Repair or replace |

# WBS Element:	2.1  High Harmonic Fast Wave (HHFW) Radio Frequency (RF) System

Component:

Function:	High Harmonic Fast Wave (HHFW) Radio Frequency  (RF) System provides plasma heating and current drive.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Plasma strike on HHFW antenna loops | Could impress high voltage on antenna loops | Plasma TV | Plasma striking the antenna loops is prevented by Faraday shields |
| Faraday shield HHFW antenna loop ablated by severe plasma strike | Could impress high voltage on antenna loops | Plasma TV | In the unlikely event of a Faraday shield failure, current flowing on the transmission line inner conductor is prevented from getting out of the Test Cell area by the antenna's DC breaks |
| HHFW antenna's inner conductor DC breaks short out | Could impress high voltage on transmission line(s) center conductor(s) | Ground fault detector, routine vacuum vessel Hi-pot | Shunted via chokes between the inner and outer conductors in the antenna's Tuning and Matching components |
| HHFW antenna's outer conductor DC breaks short out | Could impress high voltage on transmission line(s) outer conductor(s) | Ground fault detector, routine vacuum vessel Hi-pot | Shunted via grounding cables connecting transmission lines outer conductors to building steel and grounding mats along lines' entire path |
| HHFW RF power transfer switch atop the RF Enclosure in the MockUp Building in ENABLED (unsafe) position while personnel are in the Test Cell | Could direct RF power into the Test Cell | NSTX Hardwired Interlock System (HIS) | HIS monitors the positions of all D-Site RF transfer switches and imposes RF global E-STOP should any switch be in the ENABLED position during access to the NSTX Test Cell. |

WBS Element:	2.1  High Harmonic Fast Wave (HHFW) Radio Frequency (RF) System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Mechanical damage punctures outer conductor of HHFW transmission line | Possible RF radiation exposure of personnel in vicinity of puncture | Pressure switches in transmission lines | The HHFW hardwired control system monitors gas pressure in the transmission line. It automatically prohibits rf pulsing should the pressure in any line drop below its set point |
| HHFW transmission line flange not tightened after servicing | Possible RF radiation exposure of personnel in vicinity of loose flange | Standard test procedure | RF radiation survey is performed whenever the transmission lines are serviced. The survey is also performed annually. Any leaks are immediately repaired |
| Anode DC-blocking capacitor in HHFW high power amplifier shorts out | Could impress high voltage on transmission line center conductor | High Voltage Power Supply (HVPS) over-current interlocks | Shunted via chokes between the inner and outer conductors in the amplifiers' output transmission lines |
| Lightning strike or other phenomena that may cause difference in potential between D-Site and C-Site building steel | Could impress high voltage on Control wiring from D-Site to C-Site | None | In the event that an appreciable difference in potential occurs between the building steel at each Site, gas-filled spark gaps limit "touch" potential to < 15 volts at either end of the control wiring. |

WBS Element:	2.1  High Harmonic Fast Wave (HHFW) Radio Frequency (RF) System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Unplanned loss of AC power at D-Site | Possible loss of coordination between D-Site RF transfer switches and NSTX Test Cell access state | NSTX Hardwired Interlock system (HIS) and HHFW local control system | A loss of AC power at D-Site causes a loss in the "NOT E-STOP" Hardwired Interlock System signal to the HHFW System. This automatically precipitates an Emergency Stop to the HHFW System, opening all of its high voltage power supply circuit breakers |
| Unplanned loss of water to NTC HHFW Antenna | Possible thermal stress or failure to HHFW antenna | RF PLC | Loss of water in NTC causes RF controls to inhibit high power RF pulsing |

# WBS Element:	2.2  Coaxial Helicity Injection (CHI ) System

Component:

Function:	The Coaxial Helicity Injection (CHI) Current Drive System provides non-inductive plasma current drive by providing a potential difference between the center stack casing and the outer vacuum  and injecting a current. Components involved are the CHI buswork, the lower inboard and outboard PFCs (which act as electrodes, see WBS 1.1), the CHI power supply (see  WBS 5) and the lower dome gas injection systems (see WBS 3.4). Only the buswork is covered in this section. The buswork is also used to carry current during ohmic heating of the center stack casing during bakeout operations.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Blockage or leakage of cooling water circuit during normal operations | Reduction in cooling water flow in water circuit involving CHI and other water cooled cable conductors in same water circuit, reduction in rate of cooling, possible ground fault | Flow switches which are interlocked to prevent power supply operation, ground fault detection | Shutdown normal operations and restore integrity of coolant passage. |
| Blockage or leakage of cooling water circuit during bakeout | Reduction in cooling water flow in water circuit involving CHI and other water cooled cable conductors in same water circuit, reduction in rate of cooling, possible overheating of bus due to latent heat from center stack casing | Flow switches which are interlocked to prevent power supply operation, visual inspection | Shutdown bakeout operations and restore integrity of coolant passage. |

# WBS Element:	2.2  Coaxial Helicity Injection (CHI ) System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Electrical failure of insulation | If line to line, CHI power supply short circuit, overcurrent, large forces, heating, arcing, burning; if line to ground, CHI ground fault, small fault current, limited heating and burning of insulation. | Power supply system overcurrent and ground fault detection. | Shutdown, repair if possible, or replace. |
| Failure of structural support due to electromagnetic loads during normal operation | Possible open circuit, joint resistance heating, arcing, melting, possible ground fault, possible diversion of current into other metallic path(s). | Improper circuit electrical function and/or ground fault, visual inspection of impending condition during maintenance | Shutdown, repair if possible, or replace. |

# WBS Element:	2.3 Electron Cyclotron Heating (ECH) System

Component:

Function:	The ECH System provides pre-ionization of the plasma fuel gas to facilitate avalanche breakdown and inductive current drive by the OH loop voltage.  The ECH power supply and all waveguide/launcher components are located in the NSTX Test Cell. The input 480V AC circuit breaker is interlocked with the Hardwired Interlock System and Test Cell access control.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Fail to deliver RF power on receipt of trigger signal from central control system | Loss of preionization function, reduced plasma performance | Transient digitizer analysis | Troubleshoot and repair |
| Delivery of RF power outside time window of trigger signal | If during pulse, minor deviation from expected auxiliary heating profiles, if outside pulse window (in vacuum) possible overheating of internal vacuum vessel wiring or damage to sensitive diagnostics | Transient digitizer analysis, RGA analysis | Troubleshoot and repair |
| Electrical breakdown of DC break | If CHI operations with outer vacuum vessel energized, ground fault for CHI power supply, small fault current flow through waveguide, arcing, burning, melting. Otherwise, ground loop eddy currents and very minor magnetic field perturbation. | If CHI operations , power supply ground fault detection. Otherwise, detected at time of next vacuum vessel hipot. | Repair if possible or replace |

WBS Element:	2.3 Electron Cyclotron Heating (ECH) System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Launcher/window vacuum leakage | Depending on leak, possible interruption of operations | Pressure instrumentation, rate of rise measurements | Depending on leak rate, shutdown, vent vacuum vessel, repair or replace |
| RF leakage from power supply enclosure or waveguide | RF energy outside waveguide in test cell, possible malfunction of nearby electrical equipment | Periodic RF surveys | Repair waveguide/shielding |
| Unplanned loss of water to ECH source equipment | Possible thermal stress or failure of ECH klystrons | RF PLC | Loss of water in NTC causes RF controls to remove high voltage from ECH klystrons |
| Attempted energization of ECH during personnel access in the Test Cell | Possible RF radiation exposure of personnel in Test Cell | NSTX Hardwired Interlock System (HIS) | HIS monitors status of the ECH PI 480VAC and imposes an RF global E-STOP should it be ENABLED during general personnel access in the NSTX Test Cell. |
| 480V AC main input circuit breaker failure to close | Unable to operate ECH | EPICs Process Control | De-energize AC input power at higher level, access NTC, troubleshoot and repair |
| 480V AC main input circuit breaker failure to open | Indication to Hardwired Interlock System (HIS) preventing normal means of access to NSTX Test Cell (NTC) | HIS “unsafe” indication | De-energize AC input power at higher level, access NTC, troubleshoot and repair |
| Leakage of Dielectric Fluid from HV Tank | Fluid contained in collection tray with hose-connection to drum below, possible electrical breakdown if significant quantity lost | Maintenance inspection, or functional failure if significant quantity lost | Repair leak and/or electrical components |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System				Component:		General

Function:	The NBI System provides plasma heating via one TFTR beam line, consisting of three ion sources, injecting 80keV neutral particles at 5MW, for pulses of 5 second duration, into the NSTX plasma. In addition, brief (50mS) conditioning pulses are performed between NSTX machine discharges, without plasma, with the NBI power being deposited on the protective plates..

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Misoperation of Accel Power System, or Auxiliary Power System, Ion Sources, Beam Line Accelerating Systems, or Control System, NBI power waveform does not conform to pre-programmed request. | One or more ion sources fails to deliver intended power vs. time to plasma. | Physics waveforms | Troubleshoot and repair. Depending on cause of fault, could require access to NTC. |
| Misoperation of Control System, NBI power is injected outside of normal intended time interval. | Unintended NBI power is deposited on protective plates, possible overheating. | Physics waveforms | Troubleshoot and repair. |
| Failure of plasma permissive interlock, NBI occurs in absence of plasma. | Unintended NBI power is deposited on protective plates. | Physics waveforms | Troubleshoot and repair. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System		Component:		NBI Duct

Function:	The NBI Duct provides a means for connection to the NSTX vacuum vessel. Equipment consists of the flange connections to vacuum vessel, bellows assemblies and flanges, Torus Isolation Gate Valve (TIV), ceramic insulator assembly and flanges (on NSTX side of TIV), and protective scraper plates to protect the duct wall and TIV from beam divergence. The TIV provides a vacuum seal for the NBI at atmosphere with NSTX at vacuum, or vice-versa. Actuation time from open to closed position, or vice-versa, is 30 seconds.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Excessive deformation of structural materials | Depending on extent, could involve buckling of duct, and/or vacuum leak, possible interruption of operations; in case of major vacuum leak, will result in automatic closure of TIV. | Pressure instrumentation, rate of rise measurements | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Failure of structural materials or welds | “ | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Failure of vacuum seal connections | Vacuum leak, possible interruption of operations | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Electrical breakdown of ceramic insulator | If CHI operations, ground fault for CHI power supply, small fault current, arcing, burning. Otherwise, ground loop eddy currents and very minor magnetic field perturbation. | If CHI operations , power supply ground fault detection. Otherwise, detected at time of vacuum vessel hipot. | Depending on leakage resistance, and need to operate CHI, shutdown, vent NSTX, repair. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System		Component:		NBI Duct (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| TIV Failure to Fully Open | Beam pathway to torus is partially or totally blocked preventing NBI operations. | No “beam ready to arm” indication | Troubleshoot and repair, depending on failure, could require venting NSTX. |
| TIV Failure to Fully Close | Inability to seal NB duct and beam line from NSTX vacuum vessel. | Ion gauges read pressures from vessel activity | Troubleshoot and repair, depending on failure, could require venting NSTX. |
| TIV Excess leakage across valve | “ | Ion gauges read pressures from vessel activity | Troubleshoot and repair, depending on failure, could continue operations via vacuum pumping and cryopumping on NBI side of valve, could require venting NSTX. |
| TIV Excessive leakage across valve during TMB operation | Very small amounts of TMB may be pumped on cryopanels if GDC extinguishes | Ion gauges reading increase during He pre-glow period in TMB procedure. | Halt TMB procedure. Cycle/repair valve or suspend TMB operation. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System			Component:	NBI Vacuum Vessel

Function:	The NBI Vacuum Vessel provides the main vacuum envelope for the NBI Beam Line Accelerating Systems, and the NBI Cryopumping systems.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Excessive deformation of structural materials | Depending on extent, could involve buckling of duct, and/or vacuum leak, possible interruption of operations; in case of major vacuum leak, will result in automatic closure of TIV, possible fast regeneration of cryopumping system (see FMEA entry for NBI Cryopumping System). | Pressure instrumentation, rate of rise measurements | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Failure of structural materials or welds | “ | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Failure of vacuum seal connections | Vacuum leak, possible interruption of operations, possible fast regeneration of cryopumping system (see FMEA entry for NBI Cryopumping System). | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System		Component:	Beam Line Acceleration System

Function:	The Beam Line Accel System consists of the Ion Sources, Neutralizers, Deflection Magnets, Ion Dumps, Beam Scrapers, and the Calorimeter, and the associated water cooling system.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Incorrect aiming of beamline and/or abnormal divergence. | Impingement of beamline onto duct scrapers and/or protective plates in duct, local melting/sputtering of metallic surfaces. | Thermocouple monitoring | Steering alignment |
| Ion Source filament, arc, or accel grid misoperation. | Reduced generation of beam current; affected power supply shutdown, but continued operation of other ion sources. | Source waveforms | Troubleshoot and repair; if source hardware failure involved, repair or replace affected source during maintenance period. |
| Neutralizer misoperation | Reduced neutralization, excess ion current, mismatch with deflection magnet current, ions are not efficiently deflected onto the ion dump but are sprayed on to the beam scrapers in the beam box and duct, local melting/sputtering of metallic surfaces. | Ion gauge waveform abnormal, loss of beam ready to arm due to magnet power supply controller | Reset bending magnet, repair beamline if required |
| Ion deflection magnet misoperation | Ions are not efficiently deflected onto the ion dump but are sprayed on to the beam scrapers in the beam box and duct, local melting/sputtering of metallic surfaces. | Ion gauge waveform abnormal, loss of beam ready to arm due to magnet power supply controller | Reset bending magnet, repair beamline if required |
| Loss of water cooling system to one or more beam line components | Low flow and/or high water exit temperature to affected component, NBI shutdown via interlocks, possible freezing of water lines, possible leak (see next FMEA entry). | Flow and temperature interlocks. | Troubleshoot and repair; if beam line hardware failure involved, repair or replace affected components during maintenance period. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System	Component:	Beam Line Accel System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Water leak from ion source, ion dump, calorimeter, beam scraper, neutralizer, or deflection magnet. | Depending on size of leak, vacuum vessel pressure rise; shutdown of water system;, water condensation on cryopanels; cryopumping system shutdown; possible fast regeneration of cryopumping system (see FMEA entry for NBI Cryopumping System);possible closure of TIV, possible opening of pressure relief valve; discharge of water into local containers. | Pressure instrumentation, rate of rise measurements | Repair or replace component(s) during maintenance period. |
| SF6 leak in NTC or NBI Power Conversion Building | SF6 detectors sound alarm and close valves on SF6 supply skid, small quantity of SF6 released. | SF6 detectors | Shutdown NBI operations and repair leak. |
| SF6 leak into ion source. | Ion source misoperation and shutdown; possible closing of source isolation valve. If valve remains open, SF6 is trapped on cryopanels and subsequently pumped from machine when panels are regenerated. If valve closes, gas is pumped out via source roughing system. | Poor base pressure, rate of rise in source during regens, poor source performance | Repair or replace affected ion source during maintenance period |
| Calorimeter failure to raise | Beam pathway to torus is partially or totally blocked preventing NBI operations. | No ready to arm, no beam | Troubleshoot and repair; if necessary repair or replace affected assembly during maintenance period via venting of NBI vacuum vessel. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System	Component:	Beam Line Accel System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Calorimeter failure to lower | Inability to perform beam power calibration shots. | No ready to arm, no beam | Troubleshoot and repair; if necessary repair or replace affected assembly during maintenance period via venting of NBI vacuum vessel. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System		Component:	Cryopumping System

Function:	The cryopumping system assists the active pumping systems to maintain high vacuum in the NBI vacuum vessel and duct, and the NSTX vacuum vessel, via cryocondensation on to liquid helium (LHe) cooled panels guarded by liquid nitrogen (LN2) cooled panels. System consists of the LHe and LN  refrigeration systems, piping systems, and cryopanels in the NBI vacuum vessel.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Cryopumping system, cryogen supply low flow or high inlet temperature. | Depending on nature/extent of reduction in supply, reduction in cryopumping effectiveness; possible NBI shutdown; possible regeneration (boil off) of absorbed gases (exhausted by vacuum pumping systems); possible fast regeneration of cryopumping system (see FMEA below). | Operator annunciated fault condition by PLC, security, and procedural phone calls to cog engineer | Operator adjustments, repair refrigerator. |
| Fast regeneration of Cryopumping System. | Rupture of pressure relief (burst) disks external to NBI vacuum vessel box, inside NTC; cryogen supply valves will close; cryogenic vapors will be released into NTC; boil-off of condensed gases from cryopanels, will be released to vacuum vessel and exhausted by vacuum pumping system; NBI TIV will close. | Operator annunciated fault condition by PLC, security, and procedural phone calls to cog engineer | Operator adjustments, repair refrigerator. |

# WBS Element:	2.4   Neutral Beam Injection (NBI) System		Component:	Cryopumping System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| High H concentration in pumping exhaust during regeneration | Potential explosion hazard | Vacuum gauge reading during regenerations | Pump out lines |
| Cryogenic line inward leakage to vacuum jacketed supply lines and condensation of oxygen | Potential explosion hazard. | Loss of thermal resistance of jacket, excess temperature rise of cryogens. | Pump out lines |
| Cryogenic line rupture external to NBI vacuum vessel. | Release of cryogenic fluid and vapor into NTC, cryogen supply valves will close, NBI TIV will close, fast regeneration will occur (see prior FMEA entry). | Plumes | Repair lines |
| Cryogenic line rupture internal to NBI vacuum vessel. | Release of cryogenic fluid and vapor into NBI vacuum vessel, cryogen supply valves will close, NBI TIV will close, fast regeneration will occur (see prior FMEA entry). | Ion gauge | Vent beamline, repair leak, or replace beamline cryo panels |

WBS Element:	2.4   Neutral Beam Injection (NBI) System			Component: Local PLC Controller

###### Function:	Provides PLC based operator interface and interlocks for NBI equipment protection

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of PLC functionality | Shutdown of NBI, all power supply systems, valves and pumps revert to safe state, interruption of machine operations | Status signals to EPICS Process Control System and PLC monitor | Troubleshoot and repair |
| PLC I/O failure | Loss of action/reaction confirmation, PLC alarm condition | PLC logic | Troubleshoot and repair |

# WBS Element:	3.1 Vacuum Pumping System

## Component:		Main Pumping Duct

Function:	The main pumping duct, consisting of flange connection to vacuum vessel, bellows assembly and flanges, ceramic insulator assembly and flanges, as well as tee ducts and flanges for connections to TMP and Roughing isolation valve assemblies, provides the physical means for connection of the pumping system to the vacuum vessel, as well as provision for interface of diagnostics and vacuum pumping I&C (including the Residual Gas Analyzer (RGA)).

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Excessive deformation of structural materials | Depending on extent, could involve buckling of duct, and/or vacuum leak, possible interruption of operations | Pressure instrumentation, rate of rise measurements | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Failure of structural materials or welds | “ | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Failure of vacuum seal connections | Vacuum leak, possible interruption of operations | “ | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Electrical breakdown of ceramic insulator | If CHI operations with outer vacuum vessel, ground fault for CHI power supply, small fault current, arcing, burning. Otherwise, ground loop eddy currents and very minor magnetic field perturbation. | If CHI operations , power supply ground fault detection. Otherwise, detected at time of next vacuum vessel hipot. | Shutdown, vent vacuum vessel, repair if possible or replace |

WBS Element:	3.1 Vacuum Pumping System

## Component:		Turbomolecular Pumps 	(TMP)

Function:	The Turbomolecular Pumps (TMP) and associated duct, bellows, isolation valve, backing valve, and flange which connects to the main pumping duct provide the high vacuum pumping of the vacuum vessel.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Vacuum leak on duct side of isolation valve | Vacuum leak, possible interruption of operations | Pressure instrumentation, rate of rise measurements | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Vacuum leak on pump side of isolation valve | Vacuum leak, possible interruption of operations, or reduced pumping speed | “ | Close valve, repair leak |
| Isolation valve closed, vacuum leak across isolation valve seat | Depending on leak rate and state of TMP, possible interruption of operations | Pressure instrumentation | Depending on leak rate, back fill TMP volume with He, or shutdown, vent vacuum vessel, repair |
| Isolation valve fail to close | No immediate effect | PLC logic | Troubleshoot and repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Isolation valve fail to open | Reduction in pumping capability, reduced performance | PLC logic | Troubleshoot and repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |

WBS Element:	3.1 Vacuum Pumping System		Component:		Turbomolecular Pumps (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| TMP failure (fail to start, or trip) | Reduction in pumping capability, reduced performance | TMP instrumentation and/or PLC logic | Close isolation valve, backfill TMP volume with N2, repair |
| TMP foreline valve fail to open | Loss of TMP and reduced pumping speed and possible interruption of machine operations | PLC logic | Close all TMP isolation and backing valves, repair |

WBS Element:	3.1 Vacuum Pumping System

## Component:		Roughing Pump Skid

Function:	Roughing Pump Skid and associated duct, bellows, isolation valve, nitrogen vent valve, and flange connect to the main pumping duct to provide rough pumping of the vacuum vessel. Note: The roughing pump skid is shared with the NBI system, and is controlled by the NBI PLC.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Vacuum leak on duct side of isolation valve | Vacuum leak, possible interruption of operations | Pressure instrumentation, rate of rise measurements | Provide temporary repair in situ if possible, otherwise shutdown, vent vacuum vessel, repair |
| Vacuum leak on pump side of isolation valve | “ | “ | Close valve, repair leak |
| Isolation valve closed, vacuum leak across isolation valve seat | Depending on leak , possible interruption of operations | Pressure instrumentation | Depending on leak rate, back fill TMP volume with He, or shutdown, vent vacuum vessel, repair |
| Isolation valve fail to open | Rough pumping not available, pump down and machine operations precluded | PLC logic | Troubleshoot and repair |
| Isolation valve fail to close | Transition from rough pumping to high vacuum pumping not possible, machine operations precluded | PLC logic | Troubleshoot and repair |

WBS Element:	3.1 Vacuum Pumping System

## Component:		Backing Pump Skid

Function:	Backing Pumps and associated duct, nitrogen vent valve, and flange connect to the TMPs backing isolation valve to provide low pressure conditions on back side of TMPs.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Vacuum leak in foreline | Possible interruption of operations | Pressure instrumentation, rate of rise measurements | Close TMP backing isolation valve and TMP foreline valves, backfill TMPs with N2, repair leak |
| Pump failure (fail to start, or trip) | High vacuum pumping precluded, interruption of operations | Pressure instrumentation and/or PLC logic | Close isolation valve, backfill TMP volume with N2, repair |
| Backing skid valve fails to open | TMP operations precluded, interruption of NSTX operations | Pressure instrumentation and/or PLC logic | Backfill TMP with N2 and repair |

WBS Element:	3.1 Vacuum Pumping System

## Component:		N2 Vent Valves

Function:	Provide connections to N2 source for backfilling TMP, Backing, and Roughing volumes

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| N2 Vent Valve of TMP system leaks or fails to stay closed | Automatic isolation of effected system, possible interruption of operations | Pressure instrumentation and PLC monitor | Troubleshoot and repair |
| N2 Vent Valve of Backing system leaks or fails to stay closed | Automatic isolation of effected system, possible interruption of operations | Pressure instrumentation and PLC monitor | Troubleshoot and repair |
| N2 Vent Valve of Roughing system leaks or fails to stay closed | Automatic isolation of effected system, possible interruption of operations | Pressure instrumentation and PLC monitor | Troubleshoot and repair |

WBS Element:	3.1 Vacuum Pumping System

## Component:		Vacuum Pumping System Local I&C

Function:	Provides PLC based operator interface and interlocks for VPS equipment protection

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of PLC functionality | Shutdown of VPS, all valves and pumps revert to safe state, interruption of machine operations | Status signals to EPICS Process Control System and PLC monitor | Troubleshoot and repair |
| PLC I/O failure | Loss of action/reaction confirmation, PLC alarm condition | PLC logic | Troubleshoot and repair |

WBS Element:	3.1 Vacuum Pumping System

## Component:		Residual Gas Analyzer (RGA)

Function:	Analysis of content of residual gasses.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Measurement head failure | Temporary loss of RGA functionality | Loss of signal and status from RGA monitor | Revert to installed spare measuring head |
| RGA monitor failure | Loss of RGA functionality, loss of information to machine operators | Loss of signal and status from RGA monitor | Troubleshoot and repair |

# WBS Element:	3.2 Cooling Water System

## Component:		Water Distribution in Test Cell

Function:	Distributes water from main manifolds to NSTX coils, coil leads, and detects loss of flow

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Coil water circuit leak, supply side hose | Reduction/loss of flow to coil; large leak would result in flow into floor drain system, eventually to TFTR Liquid Effluent Collection (LEC) tank | Depending on extent of leak, flow switch dropout, or low tank level, and PLC logic response (loss of flow removes PAUX permissive from power supply system, low tank level causes operator alarm) | Shutdown and repair |
| Coil water circuit leak, return side hose | Large leak would result in flow into floor drain system, eventually to TFTR Liquid Effluent Collection (LEC) tank | Depending on extent of leak, flow switch dropout, or low tank level, and PLC logic response (loss of flow removes PAUX permissive from power supply system, low tank level causes operator alarm) | Shutdown and repair |
| Coil connection hose electrical breakdown | Small leakage current to ground (limited by high resistance grounding) | Depending on failure, maintenance inspection & test (Megger/hipot), ground fault detected by power supply system ground fault detector | Troubleshoot and repair |

WBS Element:	3.2 Cooling Water System		Component:		Water Distribution (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Piping water leak | Water dripping on floor, possible reduction/loss of flow; large leak would result in significant flow into floor drain system and rapid reduction in tank level | Maintenance inspection, or low flow switch flow, or low tank level, and PLC logic response (loss of flow removes PAUX permissive from power supply system, low tank level causes operator alarm) | Shutdown and repair |
| Venturi sensor tubing leak, low pressure side | Venturi pressure independent of flow, false indication of flow | PLC logic checks that all flow switches are dropped out prior to energizing pumps (not detected until pumps are de-energized) | Troubleshoot and repair |
| Venturi sensor tubing leak, high pressure side | Venturi pressure independent of flow, false indication of low flow | PLC logic response as if low flow (remove PAUX permissive from power supply system) | Troubleshoot and repair |

WBS Element:	3.2 Cooling Water System		Component:		Water Distribution (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Flow switch stuck open | False indication of low flow | PLC logic response (removes PAUX permissive from power supply system) | Troubleshoot and repair |
| Flow switch stuck closed | False indication of adequate flow | PLC logic checks that all flow switches are dropped out prior to energizing pumps (not detected until pumps are de-energized) | Troubleshoot and repair |

WBS Element:	3.2 Cooling Water System

## Component:		Pumps & Automatic Valves

Function:	The Low Pressure Pump provides cooling water flow, the High Pressure Pump (and redundant back-up unit) boosts the pressure for the OH coil. The Automatic Supply and Return Valves control the overall supply of cooling water to the NTC.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Low Pressure Pump failure | Loss of coolant flow to NTC | Flow switch measurements, de-energize PAUX relay to power supply system permissives | Shutdown and repair or replace |
| High Pressure Pump failure | Loss of OH pressure, reduction of OH coolant flow | Flow switch measurements, de-energize PAUX relay to power supply system permissives | Switch to back-up unit |
| Automatic Supply Valve failure to open | Delivery of coolant to NTC precluded, PLC logic prevents starting of pumps | PLC logic | Troubleshoot and repair or shutdown and replace |
| Automatic Supply Valve failure to close | Loss of ability to isolate NTC water circuits from pump room, PLC logic prevents closing of Automatic Return Valve | PLC logic | Close manually, troubleshoot and repair or shutdown and replace |
| Automatic Return Valve failure to open | Delivery of coolant to NTC precluded, PLC logic prevents opening of Automatic Supply Valve | PLC logic | Troubleshoot and repair or shutdown and replace |
| Automatic Return Valve failure to close | Loss of ability to isolate NTC water circuits from pump room | PLC logic | Close manually, troubleshoot and repair or shutdown and replace |

WBS Element:	3.2 Cooling Water System

## Component:		Auxiliary Components

Function:	The D-site HVAC cooling system provides chilled water for removing heat from the coil cooling water and the Vacuum Pumping skids. The Deionizing System maintains high coil cooling water resistivity. Filters remove particulate from the coil cooling water system. Dew Point Detection System prevents operation of coils below dew point temperature.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| D-site HVAC cooling system failure | Loss of chilled water, loss of cooling of Vacuum Pumping System, interruption of operations | Vacuum Pumping System PLC loss of cooling water flow alarms, Cooling water PLC high temperature alarm, interlocked with PAUX relay to power supply system permissives | Shutdown and repair |
| De-ionizing System failure | Gradual decrease in cooling water resistivity, possibly leading to ground fault, small leakage current to ground | Daily hipot of coils prior to energization, power supply system ground fault detection | Troubleshoot and repair |
| Blockage in filters | Reduced coolant flow, possibly leading to drop out of flow switches, interruption of operations | Pressure drop across filters is monitored by water system operators | Perform maintenance |
| Dew Point Detection System failure | Inaccurate dew point indication, possible condensation on coils, possible ground fault, small leakage current (limited by high resistance grounding), redistribution of voltage to ground, Level 1 power supply fault (suppress/bypass) | PLC logic indicating input out of normal range, power supply system ground fault detection | Troubleshoot and repair |

WBS Element:	3.2 Cooling Water System

## Component:		Cooling Water Local I&C

Function:	PLC system monitors flow switches, valve positions, temperatures, etc., provides interlocks to ensure proper sequence of operations and configuration, and provides interlock to Power Supply System PAUX relay which is required to issue power supply permissive to energize the coils.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of PLC functionality | Interruption of machine operations, PAUX relay drops out due to loss of “keep alive”. State of water system components depends on failure scenario, all components could stay in last commanded state | Status signals to EPICS Process Control System and drop out of PAUX relay to power supply permissive interlock | Manually position all valves and pumps set to safe state, troubleshoot and repair |
| PLC I/O failure | Loss of action/reaction confirmation, PLC alarm condition | PLC logic | Troubleshoot and repair |

# WBS Element:	3.3 Bakeout System

Component:

Function:	The Bakeout system heats the plasma facing components (PFCs) and vacuum vessel (VV) to elevated temperatures (350oC and 150oC respectively) for cleaning, and provides heating and cooling during operations. The use of the bakeout system for day 2 operations will be limited to 150C max, with water as the heat exchange fluid.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of Heater Power | Loss of heat input to VV and PFCs | Thermocouples on NSTX machine | Troubleshoot and repair |
| Failure of Pump in High Temperature Loop | Loss of heat input to VV and PFCs | Over-temperature switch trips off heater | Troubleshoot and repair |
| Failure of Pump in Low Temperature Loop | Loss of heat removal from VV and PFCs | Thermocouples on NSTX machine | Shutdown all heat inputs, troubleshoot and repair |
| Leak in Pipeline inside Vacuum Vessel | Heat exchange fluid released into VV | Residual Gas Analyzer | Vent VV and repair leak |
| Leak in Pipeline outside Vacuum Vessel | Heat exchange fluid released into NSTX Test Cell, possible injury to personnel if in contact with hot liquid | Expansion tank level detection | Repair leak |
| Blockage in Pipeline | Uneven heating and/or cooling | Thermcouples on NSTX machine and IR Camera | If inside, vent VV and remove blockage, if outside, remove blockage |
| Loss of Nitrogen blanket in Expansion Tank | Expansion Tank level rises | Expansion tank level detection | Repair leak and restore blanket |
| Reduction of HVAC cooling water flow and/or excess cooling water temperature | Reduction in cooling capability | Bakeout Skid control panel logic, Thermocouples on NSTX machine | Shutdown all heat inputs and restore HVAC cooling water supply |

# WBS Element:	3.3 Bakeout System	(con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Failure of Temperature Controller | Temperature not per setpoint, if overtemperature, possible boiling of heat exchanger fluid, possible opening of pressure relief valve | Over-temperature switch trips off heater | Troubleshoot and repair |
| Contamination of Dielectric Break in manifolding | Loss of electrical isolation of outer VV | Hipot leakage measurements | Clean |
| Electrical breakdown of Dielectric Break in manifolding | If CHI operations with outer vacuum vessel energized, ground fault for CHI power supply, small fault current flow through manifolding to ground. Otherwise, small ground loop eddy currents and resultant magnetic field perturbation. | If CHI operation, power supply ground fault detection. | Repair if possible or replace |

# WBS Element:	3.4 Gas Delivery System	(GDS)

Component:

Function:	The Gas Delivery System  provides storage of gases and delivers prescribed quantities of same at prescribed rates in pulses which are synchronized with the NSTX facility clock system.	 In addition the system provides vacuum pumping to remove and exhaust residual gases from gas delivery lines. Control is via the Vacuum Pumping System PLC

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| TIV fails to close | Inability to isolate pulse valve from vacuum vessel | Valve status indication on PLC | Possible need to pump out and backfill volume. Troubleshoot and repair. |
| TIV fails to open | Inability to utilize injector | Valve status indication on PLC | Troubleshoot and repair. |
| Piezoelectric injection valve failure to open | Gas delivery from failed valve precluded, reduced performance | Injection volume and vacuum vessel pressure instrumentation monitored via PLC | Troubleshoot and repair if possible, or replace during vacuum opening |
| Piezoelectric injection valve failure to close, or leakage across valve | Leakage of gas from injection volume into vacuum vessel, gas delivery from failed valve precluded, reduced performance | Injection volume and vacuum vessel pressure instrumentation monitored via PLC | Troubleshoot and repair if possible, or isolate and evacuate injection volume and replace during vacuum opening |

WBS Element:	3.4 Gas Delivery System	(con’t)

Component:

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Vacuum pump failure | Inability to remove residual gases from portions of the GDS or gas injection assembly | Vacuum pump status indication, line pressure instrumentation monitored by PLC | Troubleshoot and repair |
| Failure of GDS pumpout valve | Inability to remove residual gases from portions of the GDS or gas injection assembly | Vacuum pump status indication, line pressure instrumentation monitored by PLC | Troubleshoot and repair. |
| Leakage in GDS due to faulty welds or leaky fittings | Inability to achieve required vacuum in gas delivery system | Pressure instrumentation monitored via PLC | Troubleshoot and repair |
| TMB leakage due to faulty welds or leaky fittings | TMB leaking into NTC where TMB pressure > atm. pressure (typ. to Piezoelectric valves) | With handheld gas leak detector or thermal imager, or inability to hold pressure in system. | Close all remotely actuated valves. Attempt to isolate leak. If safe, wearing SCBA close TMB cylinder valve. |
| Gas cylinder or supply piping leak, due to faulty valve or fittings | Release of gas into NTC | Loss of gas pressure monitored via PLC | Repair or replace |
| TMB Gas cylinder or supply piping leaking due to faulty valve or fittings | TMB leaking into NTC where TMB pressure > atm. pressure | With handheld gas leak detector or thermal imager or inability to hold pressure in system. | Close all remotely actuated valves. Attempt to isolate leak. If safe, wearing SCBA close TMB cylinder valve. |
| Lower Dome Gas Injection System, excess gas pressure in forelines involving ceramic insulator break between center stack casing and ground | Electrical breakdown across ceramic, arcing, burning, melting | Pressure instrumentation monitored via PLC and interlocked with CHI power supply permissive | Repair/replace/adjust malfunctioning components |

WBS Element:	3.4 Gas Delivery System	(con’t)

Component:

| Lower Dome Gas Injection System, excess gas prefill pressure in injection reservoir | If not detected, excess gas would be admitted to vacuum vessel leading to reduced dielectric strength across various ceramic insulator gaps | Pressure instrumentation monitored via PLC and interlocked with CHI power supply permissive | Repair/replace/adjust malfunctioning components |
| --- | --- | --- | --- |
| Failure of Portable Gas Leak Detector for TMB | Unable to detect TMB in the NTC atmosphere | Unable to calibrate, either manually or via self-calibration. | Suspend TMB injection. Close all remotely actuated GDS valves. Trouble shoot and repair. If repair infeasible, terminate TMB injection. |
| Vent stack nitrogen purge fails | Lack of nitrogen flow in vent stack will lead to presence of air in vent stack. Possibility of fire or explosion during TMB injection if GDC is lost.. | Lack of flow in vent stack | Halt NBI or TMB operation as appropriate. Trouble shoot system. Once on line- resume normal operation. |

# WBS Element:	3.5	Glow Discharge Cleaning (GDC) System

Component:

Function:	GDC provides conditioning of the vacuum vessel and PFCs via bombardment by particles from a diffuse plasma in helium. Vacuum vessel and center stack casing will be grounded. The GDC system for 1st plasma will consist of a retractable probe attached to a portable power supply.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Short circuit between probe and vacuum vessel | GDC power supply will trip on overcurrent. No measurable potential rise of grounded vacuum vessel will occur due to limited current delivery of GDC power supply. | Loss of GDC current as indicated by GDC power supply instrumentation | Troubleshoot and repair |
| Failure of GDC power supply current limiting resistor | GDC power supply will trip on overcurrent. No measurable potential rise of grounded vacuum vessel will occur due to limited current delivery of GDC power supply. | Loss of GDC current as indicated by GDC power supply instrumentation | Troubleshoot and repair |
| Incorrect helium pressure | GDC current could become concentrated and sputter metallic impurities onto PFCs leading to loss of conditioning | Visible arcing | Increase pressure to reduce arcing and achieve uniform GDC |
| GDC probe stuck | If stuck in retracted position, unable to perform GDC, if in extended position, unable to resume normal NSTX operations | Local probe position indication | Remove actuator, bellows enclosure, withdraw probe, and repair. |
| GDC probe vacuum leak | Depending on leak, possible interruption of operations | Pressure instrumentation, rate of rise measurements | Withdraw probe, close torus interface gate valve, remove probe and repair |

# WBS Element:	3.5	Glow Discharge Cleaning (GDC) System (con’t)

Component:

| Glow stops during TMB injection. | TMB does not break down and deposit on surfaces. TMB pumps through NSTX vacuum system. Vent stack purged with nitrogen, so no possibility of combustion in vent stack. | PLC observes low GDC current and automatically shuts down TMB injection. | Restart GDC with He and return to operation. If repeated failure of system to maintain GDC, trouble shoot system up to and including aborting TMB operation. |
| --- | --- | --- | --- |

# WBS Element:	4X Diagnostics

Component:		Plasma Current Rogowski Coils					See Footnote

Function:	Two (2) Plasma Current Rogowski Coils provide redundant measurements of plasma current

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Shorted turns | Reduced voltage per unit of plasma current derivative | Difference between redundant measurements | Adjust scaling, replace coil if and when NSTX center stack removed and disassembled |
| Open circuit | Loss of signal | Difference between redundant measurements | Revert to single measurement, replace coil if and when NSTX center stack removed and disassembled |
| Groundwall insulation failure to OH ground plane | Common mode voltage electrically coupled into integrator circuitry | Noisy signal | Revert to single measurement, replace coil if and when NSTX center stack removed and disassembled |
| Groundwall insulation failure to center stack casing | If non-CHI operations or CHI operations with center stack casing grounded, common mode voltage electrically coupled into integrator circuitry. If CHI operations with center stack casing energized, fault path for CHI power system, possible destruction of coil, arcing, burning, melting of leads to integrator rack and/or integrator circuit board | If non-CHI operations or CHI operations with center stack casing grounded, noisy signal. If CHI operations with center stack casing energized, CHI power supply system ground fault and/or overcurrent detection | Revert to single measurement, replace coil if and when NSTX center stack removed and disassembled |
| Integrator failure | Signal error | Difference between redundant measurements | Troubleshoot and repair/replace |

WBS Element:	4X Diagnostics

## Component:		Flux Loops

Function:	Single turn flux loops (redundant pairs, each loop wired to instrument rack, one instrumented) installed at approx. 50 locations inside/outside vacuum vessel. Used for plasma control (shape reconstruction) and calculation of eddy currents in conducting passive structures.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Open circuit | Loss of signal | Abnormal magnetic reconstruction | Revert to spare loop, replace failed loop when accessible |
| Groundwall insulation failure to structure at same circuit common as instrumentation | Small common mode voltage electrically coupled into integrator circuitry | Noisy signal | Revert to spare loop, replace failed loop when accessible |
| Center stack flux loop (around OH coil ground plane) groundwall insulation failure to center stack casing | If non-CHI operations or CHI operations with center stack casing grounded, small common mode voltage electrically coupled into integrator circuitry. If CHI operations with center stack casing energized, fault path for CHI power system, possible destruction of loop, arcing, burning, melting of leads to integrator rack and/or integrator circuit board | If non-CHI operations or CHI operations with center stack casing grounded, noisy signal. If CHI operations with center stack casing energized, CHI power supply system ground fault and/or overcurrent detection | Diagnose extent of failure and damage, repair and replace as required. |
| Integrator failure | Signal error | Abnormal magnetic reconstruction | Troubleshoot and repair/replace |

WBS Element:	4X Diagnostics

## Component:		Thermocouples

Function:	Thermocouples (approx. 50 in vessel, 20 ex-vessel) installed on  PFC backplates, vacuum vessel, center stack casing, and OH groundwall insulation. In general, toroidal redundancy is provided (for each poloidal location, several toroidal locations are instrumented).

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Open circuit or short circuit | Loss of signal | Signal outside normal range, alarm via EPICS Process Control | Use nearby thermocouples or others in same poloidal location |
| Groundwall insulation failure to structure at same circuit common as instrumentation | Small common mode voltage electrically coupled into monitoring circuitry, signal noisy during pulse | Noisy signal during pulse | Ignore noisy signal during pulse |
| Center stack thermocouple (around OH coil ground plane) groundwall insulation failure to center stack casing | If non-CHI operations or CHI operations with center stack casing grounded, small common mode voltage electrically coupled into monitoring circuitry. If CHI operations with center stack casing energized, fault path for CHI power system, possible destruction of thermocouple, arcing, burning, melting of leads to instrument rack and/or monitoring circuitry board | If non-CHI operations or CHI operations with center stack casing grounded, noisy signal. If CHI operations with center stack casing energized, CHI power supply system ground fault and/or overcurrent detection | Ignore noisy signal during pulse. If failure, diagnose extent of failure and damage, repair and replace as required. |
| Monitoring electronics failure | Signal error | Signal outside normal range, alarm via EPICS Process Control | Troubleshoot and repair/replace |

# WBS Element:	5X Power Systems

## Component:		AC Power Systems (WBS 5.1)

Function:	AC Power Systems receives power from the 138kV utility grid and supplies all electrical power to the NTSX experiment This includes Auxiliary (House) AC Power and Experimental AC Power.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of 138kV AC power to PPPL | Interruption of NSTX operations, Vital loads supplied immediately by UPS power: - NTC Fire Protection Panel - NTC Emergency Lighting - HIS Critical loads supplied by Standby Diesel Generator after start up delay of approximately 10 seconds: - NTC Cooling Water Skids & PLC - NTC Vacuum Pumping Skids & PLC - NTC Lighting NSTX Control Room NBI Helium Refrigeration and Water Systems | Various | Await restoration of power |
| Loss of AC power to any/all components of Cooling Water System | If pumps, cooling water flow ceases; if automatic valves, valves remain in last position, all valves remain manually operable | PLC and EPICS Process Control | Await restoration of power |

WBS Element:	5X Power Systems				Component:		AC Power Systems (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of AC power to any/all components of Vacuum Pumping System and Gas Delivery System | All components revert to safe state | PLC and EPICs Process Control | Await restoration of power |
| Standby Diesel Generator failure during 138kV utility outage | All components revert to safe state. If bakeout underway, revert to alternate 26kV line to PPPL or, if 26kV not available, configure cooling water system valves to circulate municipal water supply through OH coil. Loss of power to Helium Refrigeration System; regeneration of cryopanels, possible rupture of burst disks, possible freezing of water cooling lines (see NBI FMEA). | Loss of power | Await restoration of power |

WBS Element:	5X Power Systems

## Component:		AC/DC Power Supply Converters

Function:	The AC/DC Power Supply Converters (a.k.a. Transrex power supplies) convert AC power to controlled DC power in the TF, PF, OH, and CHI circuits.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Thyristors failure to block voltage when system has been disarmed (requires that ≥ 2 Master Gate Drivers suffer spurious missfire, or ≥ 4 thyristors suffer spurious missfire without MGD pulse). Note: since the permissive relay contacts directly disable the MGD optodriver boards, control failures (firing generator, Central I&C, etc.) cannot cause this fault. | Voltage applied to output terminals, unintended flow of current in the coils if SDS line switches closed and SDS ground switches open. Will result in Level 1 fault, followed by Level 2 fault and AC breaker trip | Power supply fault detector will detect loss of permissive during pulse, (internal power supply Level 1 faults), and failure to suppress firing (Level 2 fault and AC circuit breaker trip). | Troubleshoot and repair |

WBS Element:	5X Power Systems			Component:		AC/DC Power Supply Converters (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Loss of normal thyristor gate pulse control due to: - miscellaneous power supply internal fault conditions detected by power supply fault detector - firing generator malfunction - master gate driver malfunction - loss of incoming 13.8kV - loss of 120V control power | Output voltage waveform not in accordance with PSRTC software command, load (coil) current not controllable, possible overcurrent or excessive duration of current. After detection of fault, shutdown by suppress, bypass action with delivery of additional volt-seconds to load depending on AC sine wave phase angle at time of fault initiation, possible AC feeder breaker trip. Current waveform after fault depends on time delay to suppress/bypass, phase angle at time of suppress/bypass initiation, and load inductance, as well as shutdown sequence of mutually coupled circuits | PSRTC software branch and/or load overcurrent detection, Power supply fault detector including section overcurrent, module overcurrent, and overtime detection (internal power supply Level 1 faults), Analog Coil Protection overcurrent/overtime detection, Rochester Instrument System (RIS) overcurrent and ∫i2(t)dt detection (external Hardwired Control System (HCS) Level 1 faults) , AC feeder breaker overcurrent and overtime detection | Troubleshoot and repair or swap power supplies if spare available |

WBS Element:	5X Power Systems			Component:		AC/DC Power Supply Converters (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Failure to suppress/bypass after internal Level 1 fault | Continued flow of current in converter transformer and application of voltage to load following initial fault detection, transition to power supply internal Level 2 fault state, command to trip AC feeder breaker, AC feeder breaker trip | Power supply fault detector Level 2 fault detection and AC feeder breaker overcurrent and overtime detection | Troubleshoot and repair or swap power supplies if spare available |
| Ground fault | Shift in voltage to ground around circuit, small leakage current to ground (limited by high resistance grounding), suppress/bypass per HCS Level 1 fault | Power supply system ground fault detection | Troubleshoot and repair or swap power supplies if spare available |
| CHI power supply delivers current without Btf > threshold due to control failure | None; Master Gate Drivers (MGDs) of CHI power supplies are blocked unless RIS indicates Itf > threshold | Absence of TF current above threshold and of correct polarity | Diagnose and troubleshoot |

WBS Element:	5X Power Systems

## Component:		Safety Disconnect Switches

Function:	The Safety Disconnect Switches (SDS) provide two pole no load line disconnect switches and two pole grounding switches which connect the power supply system to the load. They serve to isolate the NTC from electrical hazards due to the power supply system during access to the NTC via interlocks in the Safety Lockout Device (SLD). They include spark gaps and non-linear resistors (surge arrestors) connected to ground.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Line switch fail to open | Unable to effect normal isolation of power supply system from load, unable to place SLD in "safe" state, unable to access NTC | Limit switch detectors monitored by EPICS Process Control, HCS, SLD, and HIS | Provide alternate means of isolating energy source (e.g. rack out AC feeder breakers), troubleshoot and repair |
| Line switch fail to close | Unable to connect power supply system to load | Limit switch detectors monitored by EPICS Process Control, HCS, SLD, and HIS | Troubleshoot and repair |
| Ground switch fail to close | Unable to effect normal grounding of power supply system, unable to place SLD in "safe" state, unable to access NTC | Limit switch detectors monitored by EPICS Process Control, HCS, SLD, and HIS | Provide alternate means of isolating energy source (e.g. rack out AC feeder breakers), troubleshoot and repair |
| Ground switch fail to open | Unable to place power supply system in operating configuration (unable to "arm") | Limit switch detectors monitored by EPICS Process Control, HCS, SLD, and HIS | Troubleshoot and repair |

WBS Element:	5X Power Systems			Component:		Safety Disconnect Switches (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Line switch limit switch failure, or short or open in wiring | Disparity between status of the two limit switches mounted on the two line switch poles actuated by common pneumatic mechanism; if line switches are open and failed limit switch indicates closed, unable to place SLD in safe state, and data highlighted as erroneous on EPICs display. If line switches are closed and failed limit switch indicates open, data highlighted as erroneous on EPICs display. | Limit switch detectors are monitored by EPICS Process Control and SLD | Troubleshoot and repair |
| Ground switch limit switch failure | Error in status reported by the single limit switch mounted on the common pneumatic mechanism which actuates the two ground switch poles; if ground switches are open and failed limit switch indicates closed, SLD electrical interlock would not block transition to the safe state with switches open. If ground switches are closed and failed limit switch indicates open, could close line switches and arm power supplies with ground and short circuit on system, possible ground and overcurrent condition | If fail to indicate open, would close (audible event in FCPC building) upon venting SLD. If fail to indicate closed, ground fault and overcurrent detection, HCS Level 1 fault | Troubleshoot and repair |

WBS Element:	5X Power Systems				Component:		Safety Disconnect Switches (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Pressure switch failure, or short or open in wiring | Error in status reported by pressure switch on the pneumatic reservoir; if reservoir is vented and failed switch indicates pressure, unable to place SLD in safe state. If reservoir is not vented and failed switch indicates vented, SLD could transition to safe state with pressure remaining in reservoir. If ground or line switches changed state as a result of this pressure being available, electrical interlocks in SLD would issue an E-Stop condition, all ground switches would close, all line switches would open, and all AC feeder circuit breakers would open. | If pressure switch status stuck indicating vented condition, would report erroneous data when pressurized (would be noticed on EPICs mimic display if failure affected EPICs signal). If pressure switch status stuck indicating pressurized condition, unable to place SLD into safe state. | Troubleshoot and repair |

WBS Element:	5X Power Systems			Component:		Safety Disconnect Switches (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Ground switch fail to open | Unable to place power supply system in operating configuration (unable to "arm") | Limit switch detectors monitored by EPICS Process Control, HCS, SLD, and HIS | Troubleshoot and repair |
| Loss of contact pressure on line switch blades | High contact electrical resistance, possible arcing, melting, burning | Maintenance (mechanical adjustment and joint resistance measurement) and inspection (temperature stickers) | Troubleshoot and repair |
| Spark gap electrical breakdown | Ground fault, small leakage current (limited by high resistance grounding), redistribution of voltage to ground, Level 1 (power supply suppress/bypass) shutdown | Power supply system ground fault detection | Troubleshoot and re-adjust |
| Surge arrestor electrical breakdown (due to energy overload) | Arcing and burning within SDS metal enclosed cabinet (or, in case of CHI, within metal enclosure containing additional protection unit located in NSTX Test Cell) | Depending on cause, Power supply system ground fault detection and/or power supply overcurrent condition | Replace |
| DC Potential Transducer (DCPT) failure | Error in measurement of voltage to ground (information only signal: not used for control or interlocking) | Abnormal signal | Troubleshoot and repair |

WBS Element:	5X Power Systems

## Component:		DC Current Transducers

Function:	The DC Current Transducers (DCCTs) measure the branch currents in the power supply system, which sum to the load currents in the NSTX coils and CHI circuit. They consist of, in most cases “Halmar” zero flux non-contact transducers, and in some cases “shunts” (current viewing resistors) whose voltage drop is transmitted to ground potential using a fiber optic v/f-f/v link. The signals are received by a “Halmar Signal Conditioner” which provides buffering and fan out to the various destinations. Redundant measurements of load current provided in all cases.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Excessive drift or failure of electronics | Measurement error, possible current control error (control in PSRTC shifts to signal with largest magnitude), interruption of pulse via PSRTC or HCS Level 1 suppress/bypass shutdown | Comparison with redundant measurement in PSRTC software (alarm) and in RIS (HCS Level 1 fault) | Troubleshoot and repair |
| Loss of AC power | “ | “ | “ |

WBS Element:	5X Power Systems

## Component:		Rochester Instrument System (RIS) Fault Detector

Function:	The RIS receives the output of redundant DCCTs from the TF, OH, PF2L, and PF3U&L circuits. It compares redundant signals and performs single time constant exponential ∫i2(t)dt simulation (heating and cooling) to detect current/time overloads, and detects overcurrents. In addition it produces a signal when |Itf| exceeds a setpoint, for interlocking CHI operation.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Fail to detect DCCT discrepancy | None, detected in PSRTC | Operational diagnosis of system fault response or maintenance/test | Troubleshoot and repair |
| Fail to detect overcurrent | None, overcurrent detected in PSRTC, ACP, power supply fault detectors, AC feeder protective relaying | Operational diagnosis of system fault response or maintenance/test | Troubleshoot and repair |
| Fail to detect ∫i2(t)dt overload during pulse | None, detected in PSRTC, and backed up by overtime detection in ACP, power supply fault detectors, AC feeder protective relaying | Operational diagnosis of system fault response or maintenance/test | Troubleshoot and repair |
| Fail to detect ∫i2(t)dt overload caused by repetition rate error by operators | Abnormally high temperatures before and after pulse | EPICS alarms on cooling water outlet temperatures returning to collection manifolds | Troubleshoot and repair |

WBS Element:	5X Power Systems

## Component:		Analog Coil Protection (ACP)

Function:	The ACP receives outputs from the DCCTs, via the Halmar Signal Conditioner (HSC), and detects overcurrent and current overtime conditions.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Fail to detect overcurrent | None, overcurrent detected in PSRTC, RIS , power supply fault detectors, AC feeder protective relaying | Operational diagnosis of system fault response or maintenance/test | Troubleshoot and repair |
| Fail to detect overtime | None, detected in PSRTC, ∫i2(t)dt detection in RIS , power supply fault detectors, AC feeder protective relaying | Operational diagnosis of system fault response or maintenance/test | Troubleshoot and repair |

WBS Element:	5X Power Systems

## Component:		Ground Fault Detection

Function:	The Ground Fault Detection system monitors the current through the high resistance grounding resistors located in the SDS cabinets. The current is sensed via an electromagnetic relay as well as an electronic level detector.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Electromagnetic relay malfunction | Overall I vs. T limits based on electronic level detector only | Maintenance testing | Troubleshoot and repair |
| Electronic sensor malfunction | Overall I vs. T limits based on electromagnetic relay level only | Maintenance testing | Troubleshoot and repair |

WBS Element:	5X Power Systems

## Component:		Power Supply Real Time Controller

Function:	The Power Supply Real Time Controller (PSRTC) provides control of the voltage and current delivered by the power supply system to the NSTX coils and CHI circuit. It includes the computer processors and I/O equipment located in and associated with the “Skybolt/DAS” computer system as well as the “Power Conversion Link” (PC Link) which delivers the PSRTC commands to the individual AC/DC converters.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Delivery of excess current magnitude due to, software, computer, or I/O failure | Overcurrent (level depends on failure mechanism, circuit in question, protection settings), HCS Level 1 fault (suppress bypass), possible AC feeder breaker trip | RIS, ACP, power supply fault detector, AC feeder protective relaying | Diagnose, troubleshoot and repair if required |
| Delivery of excess ∫i2(t)dt due to, software, computer, or I/O failure | Excessive temperature rise in load (level depends on failure mechanism, circuit in question, protection settings), HCS Level 1 fault (suppress bypass), possible AC feeder breaker trip | RIS (exponential heating/cooling simulation), ACP (overtime), power supply fault detector (overtime) , AC feeder protective relaying (overtime) | Diagnose, troubleshoot and repair if required |
| Delivery of excess rms current due to operator error (repetition rate too high) | Excessive ratcheting of load temperature (level depends on failure mechanism, circuit in question, protection settings), HCS Level 1 fault (suppress bypass), possible AC feeder breaker trip | RIS (exponential heating/cooling simulation), (overtime) , AC feeder protective relaying (thermal replica) | Diagnose, troubleshoot and repair if required |

WBS Element:	5X Power Systems					Component:		PSRTC (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Delivery of command to CHI power supply without Btf > threshold due to operator, software, computer, or I/O failure | None; Special interlock is provided such that Master Gate Drivers (MGDs) of CHI power supplies are blocked unless RIS indicates Itf > threshold in appropriate direction | Absence of CHI current | Diagnose and troubleshoot |
| Delivery of OH and PF1b current combination producing excess axial force in (+) z direction (launching load) due to software or I/O failure | None; Special interlock is provided such that Master Gate Drivers (MGDs) of PF1b power supplies are blocked unless RIS indicates Ioh > threshold in appropriate direction | Absence of PF1b current | Diagnose and troubleshoot |

WBS Element:	5X Power Systems

## Component:		Hardwired Control System

Function:	The Hardwired Control System (HCS) provides interlocks which prevent misoperation/misconfiguration of the power supply systems and which interface with the overall Hardwired Interlock System (HIS). Two fault levels (1 and 3) are communicated throughout each system using both series and parallel loops, referred to as L1S, L1P, L3S, L3P.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Power Supply Arm Permissive interlock chain, one or more input contact states invalid (do not reflect true equipment state) | Possible power supply operation in invalid configuration or with equipment status not ready, possible overcurrent or ground fault on power supply system, Level 1 HCS Fault (suppress/bypass) | RIS, ACP, power supply fault detector, ground fault detector, AC feeder protective relaying | Diagnose, troubleshoot and repair if required |
| Configure Permissive interlock chain, one or more input contact states invalid (do not reflect true equipment state) | Possible SDS operation in invalid configuration, possible overcurrent or ground fault on power supply system, Level 1 HCS Fault (suppress/bypass) | RIS, ACP, power supply fault detector, ground fault detector, AC feeder protective relaying | Diagnose, troubleshoot and repair if required |
| Level 1 or Level 3 fault line, series loop short circuit results in bypass of status from power supplies to HCS | None, redundant parallel lines | Disagreement between L1S and L1P (or L3S and L3P) states. | Diagnose, troubleshoot and repair if required |
| Level 1 or Level 3 fault line, parallel loop open circuit results in disconnect of status to/from power supplies & HCS | Redundant series lines, but slower fault response of PS to HCS (approx 50 mS), disconnected power supplies go to fault state upon open circuit and report to HCS via series loop | Disagreement between L1S and L1P (or L3S and L3P) states. | Diagnose, troubleshoot and repair if required |

# WBS Element:	6X Central I&C

## Component:		EPICS Process Control System

Function:	The Experimental Physics Instrumentation and Control System (EPICS) Process Control System provides the operator interface for non-real time control and monitoring of the NSTX device

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Any failure mode | No deleterious effect on equipment or personnel safety; all NSTX systems required to be immune to failure of Central I&C in this regard. Operations will be interrupted. Information regarding status of facility, beside that reported via the HIS, may not be available to the operators. | Various | Diagnose, troubleshoot and repair if required |

WBS Element:	6X Central I&C

## Component:		MDS+ Data Acquisition System

Function:	The Modular Data Systems Plus (MDS+) Data Acquisition System provides the operator interface for diagnostics control and monitoring of the NSTX device, and provides facility for archiving experimental data

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Any failure mode | No deleterious effect on equipment or personnel safety; all NSTX systems required to be immune to failure of Central I&C in this regard. Operations will be interrupted. Information regarding status of facility, beside that reported via the HIS, may not be available to the operators. | Various | Diagnose, troubleshoot and repair if required |

WBS Element:	6X Central I&C

## Component:		Safety  System

Function:	The Safety System consists of the Hardwired Interlock System (HIS) and the Safety Lockout Device (SLD). The HIS provides permissives to the power supply, RF, and NBI systems which enable them to be configured and operated. The SLD monitors the status of the power supply system safety disconnect switches and provides a “Safe” signal only when all switches are in the safe position and the compressed air supply (which actuates the switches) has been vented.  Two search and secure loops are provided, one for the NSTX Test Cell and one for the cable spread room. These loops must be armed in order for permissives to be issued.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| HIS UPS failure | E-stop condition, permissives to power supply, RF, and NBI systems removed, search and secure loops drop out, status indications in control room not functional. | Loss of indications on HIS control panel in NSTX control room | Troubleshoot and repair |
| SLD electrical interlock failure indicating SDS ground switches in safe condition when in unsafe state | Overall SLD “Safe” status not achieved, since SDS ground switches cannot be open without air supply, and SLD”Safe” status not issued if air supply still available | EPICs Process Control in combination with SLD status indicator lamps | Troubleshoot and repair |
| SLD electrical interlock failure indicating SDS ground switches in an unsafe condition when in safe state | Unable to achieve “Safe” status required for area access | EPICs Process Control in combination with SLD status indicator lamps | Troubleshoot and repair |

WBS Element:	6X Central I&C

Component:		Safety  System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| SLD electrical interlock failure indicating SDS line switches in safe condition when in unsafe state | Loss of one level of isolation. However, permissive to power supply AC/DC converters not issued in “Safe” state. Even if AC/DC converters failed to block, closed ground switches would prevent high voltage from appearing on bus bars in NSTX Test Cell | EPICs Process Control in combination with SLD status indicator lamps | Troubleshoot and repair |
| SLD electrical interlock failure indicating SDS line switches in unsafe condition when in safe state | Unable to achieve “Safe” status required for area access | EPICs Process Control in combination with SLD status indicator lamps | Troubleshoot and repair |
| SLD electrical interlock failure indicating compressed air vented when pressure still present | Loss of one level of prevention of SDS line or ground switch changing state to unsafe position. However, electrical interlocks still in effect. In case a switch changed state, an E-stop would result. | EPICs Process Control in combination with SLD status indicator lamps | Troubleshoot and repair |
| SLD electrical interlock failure indicating compressed air not vented after venting has occurred | Unable to achieve “Safe” status required for area access | EPICs Process Control in combination with SLD status indicator lamps | Troubleshoot and repair |

WBS Element:	6X Central I&C

# Component:		Safety  System (con’t)

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| HIS interface wiring (e.g. permissive, status, search and secure, etc.) open circuit or short circuit | None, receiving end will revert to safe condition since all signals are 120VAC sourced and energized in safe state | Loss of expected 120V AC signal | Troubleshoot and repair |
| Search and secure loop relay stuck in armed position | Search and secure procedure, which first drops the loop, will reveal the deficiency | Loop does not drop when door to area is opened. | Troubleshoot and repair |

# WBS Element:	Operations

Function:	Operations personnel (Chief Operations Engineer (COE), Power Supply Engineering In Charge (EIC), and Field Coil Power Conversion (FCPC) operators) set the configuration of the power supply system and program the PSRTC.

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Programming of input data leading to excess current magnitude, ∫i2(t)dt, or duration | Fault detected by PSRTC, suppress/bypass shutdown | PSRTC | Correct programming error |
| Programming of CHI operation with incorrect Btf magnitude and polarity | None; Master Gate Drivers (MGDs) of CHI power supplies are blocked unless RIS indicates Itf > threshold | Absence of CHI current | Correct programming error |
| Programming of OH and PF1b current combination producing excess axial force in (+) z direction (launching load) due to operator error | Fault detected by PSRTC, suppress/bypass shutdown | PSRTC | Correct programming error |
| Excess applied voltage due to operator error, too many power supply sections connected in series (administrative procedures not correctly followed) | Safety Disconnect Switch (SDS) surge arrestor voltage limiting, possible surge arrestor energy overload and short circuit, short circuit on power supplies, overcurrent, suppress/bypass per HCS Level 1 fault | Power supply module and section overcurrent detection | Replace arresters |

WBS Element:	Operations (con’t)						Component:

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Voltage unbalance in parallel or antiparallel configurations due to operator error (administrative procedures not correctly followed), unequal number of power supply sections in parallel or antiparallel strings | Short circuit current circulating between antiparallel strings, possible electrical breakdown of thyristors/snubber components, suppress/bypass per HCS Level 1 fault | Power supply fault detector section and module overcurrent | Reconfigure, replace modules if damaged |
| CHI power supply connected (line switches closed) but PSRTC not in normal (plasma) mode | Pulse inhibited | PSRTC | Open switches or switch PSRTC modes |
| Upper/lower PF coil currents opposite polarity due to operator error (administrative procedures not correctly followed), incorrect SDS bus link configuration (PF1aU/L, PF2aU/L, PF3aU/L) | Repulsive instead of attractive axial forces between coils, possible mechanical damage to coil supports, coil displacement, possible coil damage | Abnormal magnetic topology and coil impedance | Reconfigure links, repair damage (if any) |

WBS Element:	Operations (con’t)						Component:

| Failure Mode | Effect | Detection | Recovery |
| --- | --- | --- | --- |
| Attempt to operate power supply system with SDS ground switches closed | None, prevented by HCS interlock | No response to command to HIS arm permissive | Open ground switches |
| Attempt to open SDS line switches under load | None, prevented by HCS interlock (power supply and configure permissives are mutually exclusive) | No response to EPICS process control command | Disarm power supplies, place HIS system into “configure” |

**** END OF FMEA ****

# Footnotes

1 During pulse, cooling is not significant and is not required

2 Flow switches are located on return manifold such that flow must pass through coil in order to reach flow switch

3 Multiple ground faults not considered herein

Maximum stored magnetic energy in any NSTX coil is 3.75 MJoule (NSTX-SRD-5X-019)

During pulse, cooling is not significant and is not required

Flow switches are located on return manifold such that flow must pass through coil in order to reach flow switch

Multiple ground faults not considered herein

Maximum stored magnetic energy in any NSTX coil is 3.75 MJoule (NSTX-SRD-5X-019)

During pulse, cooling is not significant and is not required

Flow switches are located on return manifold such that flow must pass through coil in order to reach flow switch

Multiple ground faults not considered herein

There are 8 parallel cooling water circuits; blockage of multiple circuits is not considered herein

Sources of heat are I2R losses in coil plus heat flow inward from center stack casing

During pulse, cooling is not significant and is not required

Flow switches are located on return manifold such that flow must pass through coil in order to reach flow switch

Multiple ground faults not considered herein

OH coil conductor lifetime is fatigue limited (function of number of pulses at various load levels)

Maximum stored magnetic energy in any NSTX coil is 3.75 MJoule (NSTX-SRD-5X-019)

During pulse, cooling is not significant and is not required

Flow switches are located on return manifold such that flow must pass through coil in order to reach flow switch

Multiple ground faults not considered herein

Maximum stored magnetic energy in any NSTX coil is 3.75 MJoule (NSTX-SRD-5X-019)

Note: No personnel will be present in NSTX Test Cell during ECH operations

“R-Temp” high flame temperature oil

Protective plate armor is designed to absorb 5MW-5sec without damage.

Water circulation systems use standby diesel generator power, plus an additional back-up electrical generator in case of failure of main standby diesel generator

Leakage along route from NBPC through pump room and mechanical equipment room to NTC is considered extremely unlikely due to use of all-welded piping.

Administrative procedures limit maximum allowable condensed H,. PLC control sequence includes N2 purge before and after pumping gases liberated from both routine and emergency regenerations.  These measures are taken to preclude potential development of explosive mixtures.

Very unlikely due to all-welded pipe construction.

Every NSTX coil cooling water path is equipped with a flow switch

Most likely on coil side of flow switch since venturi and subsequent connection to return manifold consists of hard piping with predominantly welded joints

Every NSTX coil cooling water path is equipped with a flow switch

“keep alive” signal is the regularly transmitted PLC scanning signal (approx. once per second) which, if not received by output module, will trip “scan loss detector” and cause PAUX  relay dropout

Personnel access to test cell will be limited to qualified personnel during bakeout; bakeout skid area will be roped off.

Hydrogen gas inventory less than 311 cubic feet  (per cylinder), insufficient volume to develop an explosive concentration in the NTC

A large variety of diagnostics are planned for NSTX. The diagnostic components evaluated herein are those which are essential for machine operations

See FMEA for Center Stack Casing (WBS 1.3.3) for electrical failure of center stack thermal insulation

SeeFMEA for Center Stack Casing (WBS 1.3.3) for electrical failure of center stack thermal insulation

See FMEA for Center Stack Casing (WBS 1.3.3) for electrical failure of center stack thermal insulation

Latent heat due to bakeout could overheat the OH coil after approx. 5 hours if water cooling is entirely absent

PSRTC shuts down circuits individually, whereas HCS faults result in common shutdown amongst mutually coupled circuits

RIS protection is applied to TF, OH, PF2L, PF3U&L only

Probability of overall event sequence leading to SLD transition to safe state with switches open is remote because, in addition to the electrical interlock, the air supply is cut off and vented and the ground switches, which require air pressure to remain open, will be forced closed by mechanical springs and will remain closed even if commanded to open.

Spark gaps are not required for NSTX but cannot be removed (built into the ground switches); they will be adjusted out of normal range of voltage

RIS coverage for TF, OH, PF2L, PF3U&L only

RIS coverage for TF, OH, PF2L, PF3U&L only

RIS coverage for TF, OH, PF2L, PF3U&L only

Kirk Keys which permit the insertion of power supplies not planned for NSTX use will be removed and stored elsewhere via administrative procedures (e.g. in the D-site Shift Supervision lock box); therefore the probability of this failure is considered to be remote

Reconfiguration of bus links is a lengthy procedure typically performed by one or more technicians under the supervision of the FCPC EIC via administrative procedures; therefore this failure mode would require incorrect action on the part of several individuals over a period of several hours. On this basis the probability of this failure is considered to be small.