Project Number:  AW-2271

Contract Number:  TW-0663

November 4, 1994

SPECIAL SPECIFICATION

SECTION 08900

GLAZED CURTAIN WALL

Page

PART 1 - GENERAL

1.01	Description Of Work	2

1.02	Quality Assurance	3

1.03	System Performance Requirements	3

1.04	Submittals	4

1.05	Warranty	4

PART 2 - PRODUCTS

2.01	Acceptable Manufacturers	5

2.02	Materials and Components	5

2.03	Fabrication	6

2.04	Finishes	6

PART 3 - EXECUTION

3.01	Installation	6

3.02	Cleaning	7

SPECIAL SPECIFICATION

SECTION 08900

GLAZED CURTAIN WALL

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	The extent of glazed curtain wall work is indicated on the Drawings and schedules.

B.	Types of glazed curtain walls required include the following:

Metal stick-framed systems with flush glass appearance.

Primary System Expanse:  Single-story and multi-bay.

C.	Primary components of glazed curtain wall work include the following, including work cross-referenced to other specification sections for requirements:

1.	Aluminum curtain wall framing system.

2.	Glass and glazing work in curtain wall and window units in the curtain wall system; refer to Division 8, Section "Glass And Glazing".

3.	Column covers, soffits, sills, trim and similar border and filler items indicated as integral components of the curtain wall system.

4.	Joint sealer work that is associated with components of the curtain wall system; refer to Division 7, Section "Sealants".

5.	Anchorages, shims, fasteners, accessories and support brackets for components of the curtain wall system.

6.	Insulation and firestopping indicated in direct relation with curtain wall system.

D.	Related Sections:  Refer to the following sections for related work:

1.	Division 6, Section "Rough Carpentry"

2.	Division 7, Section "Sealants"

3.	Division 8, Section "Glass And Glazing"

4.	Division 9, Section "Gypsum Drywall"

1.02	QUALITY ASSURANCE

A.	Drawings and Specifications:  Plans, elevations and details shown on the Drawings and requirements indicated in specifications indicate spacing of members, sizes of components as well as profile, dimensional requirements, materials, fabrication and similar design requirements for glazed curtain wall work.  Minor deviations from these requirements will be accepted in order to utilize manufacturer's standard products when, in the Sandia Designated Representative's sole judgment, such deviations do not materially detract from the design concept or intended performance.

B.	Single Source Responsibility:  Provide glazed curtain wall system for the project that is the product of a single manufacturer.

C.	Contractor Qualifications:  Glazed curtain wall shall be installed by a firm with not less than 15 successful projects in the erection of stock curtain wall systems similar to systems required for this project.

D.	Standards:  Comply with applicable provisions of the "Metal Curtain Wall, Window, Store Front and Entrance Guide Specifications Manual" by AAMA.

E.	All materials used shall not contain asbestos fibers.

1.03	SYSTEM PERFORMANCE REQUIREMENTS

A.	Load-bearing Strength (Wind Resistance):  Provide the manufacturer's stock system, adapted to the application indicated, which has been tested in accordance with ASTM E 330 to withstand at least a uniform pressure of 33 psf inward and 33 psf outward.

B.	Deflections and Thermal Movements: Provide manufacturer's stock products and system which are capable of withstanding building movements and weather exposures including wind loading, and which are capable of performing within the following limitations:

1.	Normal to wall deflection not exceeding 1/200 of the span, except 1/300 for glass supporting members.

2.	Parallel-to-wall deflections not exceeding 75 percent of glass edge clearances.

3.	Thermal movements resulting from an ambient temperature range of 120 deg. F (67 deg. C), which may cause curtain wall framing range of 180 deg. F (100 deg. C).

C.	Leakage Resistance, Water and Air:  Provide the manufacturer's standard curtain wall system that has been tested to demonstrate permanent resistance to leakages as follows with a test pressure differential of 20 percent of design loading (excluding operable window or door edge joints, if any):

1.	Air Leakage:  Not more than 0.06 cfm per sq. ft. of wall area when tested with a test pressure of 6.24 psf in accordance with ASTM E 283.

2.	Water Penetration:  No uncontrolled leakage when tested at 10 psf in accordance with ASTM E 331.

D.	Condensation Requirements:  Provide manufacturer's standard or improved thermal-break construction, tested and certified by the manufacturer, in accordance with AAMA 1502.7, with 0 deg. F (-18 deg. C) outside and 25 percent relative humidity inside, to provide condensation resistance factor (CRF) of at least 62.

E.	"U" Value:  Per ASTM C-236 to be 0.56 BTU/Hr./Sq.Ft. minimum.

1.04	SUBMITTALS

A.	Shop Drawings:  Submit shop drawings showing adaptation of the manufacturer's standard system to the project; include typical unit elevations at 1/2" scale and details at 3" scale, to show dimensioning, member profiles, anchorage system, interface with building construction, and glazing.  Indicate the section moduli of wind-load-bearing members, and calculations of stresses and deflections for performance under design loading.  Show clearly where and how the manufacturer's system deviates from contract drawings and these specifications.

B.	Product Data:  Submit manufacturer's specifications for materials and fabrication of curtain wall, and instructions and recommendations for installation and maintenance.  Include certified test reports showing compliance with requirements where a test method is indicated.

C.	Samples:  Submit samples of each type and color of aluminum finish, on 12" long sections of extrusions or formed shapes and on 6" squares of sheet or plate. Include 2 or more samples in each set, showing near-limits of variations, if any, in color and texture of finish.

Sandia Designated Representative (SDR) reserves the right to require fabrication samples showing the following:

Prime members.

Joinery.

Anchorage.

Expansion provisions.

Glazing and similar details.

Profiles.

Intersections.

1.05	WARRANTY

Provide a written warranty, signed by Contractor and Installer, agreeing to repair or replace defective materials and workmanship of glazed curtain wall work during the 5-year warranty period (see primary components listing in this section).  "Defective" is defined to include the following:

Abnormal deterioration.

Abnormal aging.

Abnormal weathering.

Glass breakage due to component or installation defect.

Failure of operational parts to function normally.

Deterioration or discoloration of finishes.

Failure of the system to meet performance requirements (including structural and infiltration).

PART 2 - PRODUCTS

2.01	ACCEPTABLE MANUFACTURERS

Available Manufacturers:  One of the following or an approved equal.

Kawneer Company, Inc.; Norcross, GA

PPG Industries, Inc.; Pittsburgh, PA

Tubelite Architectural Products, Reed City, MI

Drawings are based upon Kawneer FA-SET S.S.G (thermal) with 1" glazing.

2.02	MATERIALS AND COMPONENTS

A.	Aluminum Members:  Provide members such as extrusions, formed members, sheet and plate, of the alloy, temper and thickness recommended by the manufacturer to comply with the requirements of ASTM B 221 for extrusions, and ASTM B 209 for sheet or plate.

B.	Glazing sealants and fillers are specified in "Glass and Glazing" section, and are to be as recommended by the curtain wall manufacturer.

C.	Glass is specified in "Glass and Glazing" section.  Provide 1" nominal burglar resistant insulating glass.  Glazing assembly shall be approved for use with the curtain wall framing assembly by curtain wall manufacturer.

D.	Framing System Gaskets and Joint Fillers:  Provide the curtain wall manufacturer's standard permanent type framing system gaskets and joint fillers, depending on joint movement and sealing requirements, such as sliding joints, compression joint translation, or non-moving joints.

E.	Sealants and joint fillers are specified in "Sealants" section, both for joints within the curtain wall construction and for joints at the interface of curtain wall construction with other work.  Comply with curtain wall manufacturer's requirements.

F.	Brackets and Reinforcements:  Provide the manufacturer's standard high-strength aluminum units.  Provide non-staining, non-ferrous and compatible shims for installation and alignment of curtain wall work.

G.	Trim:  Provide matching mullion covers, column covers and trim with finish to match mullions and frames as shown on the drawings.  Or, if not shown on the drawings, provide trim where all curtain wall members abut other materials.

H.	Concealed Flashing:  Provide dead-soft 26 gage stainless steel concealed flashing, treated for and of type selected for compatibility by the manufacturer.

I.	Fasteners and Accessories:  Provide the manufacturer's standard non-corrosive fasteners and accessories that are compatible with materials used in the framing system and with exposed portions that match finish of the curtain wall system. Where movement should be expected, provide slip-joint linings of sheets, pads, shims, or washers of fluorocarbon resin or a similar material recommended by the manufacturer.

1.	Where fasteners anchor into aluminum less than 0.125" thick, provide non-corrosive pressed-in splined grommet nuts or other type reinforcement to receive fastener threads.

2.	Provide not less than three fasteners into structural members at every jamb.

J.	Firestopping Materials:  Provide mineral fiber insulation or other non-combustible materials of the nature indicated, suitable for permanent placement and complying with governing regulations.

2.03	FABRICATION

A.	General:  Fabricate curtain wall system at the manufacturer's shop to the fullest extent possible, and prior to application of finishes.  Unless otherwise indicated, provide concealed fasteners.  Make provisions to weep penetrating water and condensation to the exterior.

B.	The framing system shall provide a flush glass appearance to the outside with no vertical exterior stops.  Top and bottom glass edge shall be retained by the head and sill members.  Kawneer FA-SET S.S.G. or approved equal shall be used. Perimeter framing members shall have a face dimension of 2" (57.2).  Overall depth shall be 5-1/4" (133.4) for 1" system.  Entrance framing members shall be compatible with glass framing in appearance.  All single acting entrance frames shall include positive barrier weathering.

2.04	FINISHES

Special Coating:  An Architectural Class I Color Anodic Coating conforming with Aluminum Association Standard AA-M12C22A42/44, color to match (Select Kawneer #40 Dark Bronze).

PART 3 - EXECUTION

3.01	INSTALLATION

A.	Comply with manufacturer's instructions for protection, handling and installation of fabricated curtain wall components, with particular care and attention in preservation of applied finishes.  Discard or remove and replace damaged members.

B.	Anchor components securely in place in the manner indicated, shimming and allowing for movement resulting from changes in thermal conditions.  Provide separators and isolators to prevent corrosion and electrolytic deterioration and to prevent "freeze-up" of moving joints.

C.	Firestopping:  Clean debris from behind curtain wall during erection and provide temporary closures to prevent accumulation of debris.  Install firestopping to comply with governing regulations, and AAMA TIR-A3.  Install firestopping with securely anchored metal flanges or equivalent provisions to prevent dislocation.

D.	Glazing is specified in "Glass and Glazing" sections.

E.	Sealants and joint fillers are specified in "Sealants" section.

F.	Erection Tolerances:  Install curtain wall components plumb, level, accurately aligned and accurately located in reference to column lines and floor levels. Adjust work to conform to the following tolerances:

1.	Plumb:  1/8" in 10'; 1/4" in 40'.

2.	Level:  1/8" in 20'; 1/4" in 40'.

3.	Alignment:  Limit offset of member alignment to 1/16" where surfaces are flush or less than 1/2" out of flush, and separated by less than 2" by a reveal or protruding work; otherwise limit offsets to 1/8".

4.	Location:  3/8" maximum deviation from the measured theoretical location of any member at any location.

3.02	CLEANING

A.	Protection:  After installation, the General Contractor shall adequately protect exposed portions of aluminum surfaces from damage by grinding and polishing compounds, plaster, lime, acid, cement, or other contaminants.  The General Contractor shall be responsible for final cleaning.

B.	Clean the completed system, inside and out, promptly after erection and installation of glass and sealants, allowing for nominal curing of liquid sealants. The curtain wall installer shall advise the Contractor of proper and adequate procedures for protection and cleaning during the remainder of the construction period, so that the system will be without damage and deterioration at the time of acceptance.

C.	At the time of final acceptance, clean curtain wall system thoroughly and polish glass.  Demonstrate proper cleaning methods and materials to the SNL maintenance personnel.

END OF SECTION