SUBJECT:		CONTROL AND OPERATION OF INSTRUMENTATION NETS

PURPOSE:	To establish procedures for use of the ER's Operational Communications Nets.

REFERENCES:	RCEI 24-86

ATTACHMENTS:	1.  Communication Nets and Control Stations

2.  Prowords

3.  Phonetic Alphabet

4.  ER Function Static Call Signs and Mission Identifiers

5.  Launch Range Control

ANNEXES:	None

1.0	GENERAL

A.	The proper use of operational communications nets on the ER is as important as the proper operation of tracking and data gathering equipment.  A message that is misunderstood or incomplete can cause a hold or loss of data just as surely as can an equipment malfunction.

B.	The procedures outlined below are designed to make the nets as effective as possible.  Although these procedures are written primarily for use on the instrumentation nets, they apply to all operational nets.

2.0	PROCEDURE

A.	Each net must have a net control station (NCS) with responsibility for all traffic and procedures on the net.  A list of operational nets and net controllers is included in Attachment 1.

B.	Proper identification of the calling station and the called station should preface each transmission.  Radio call signs detailed in the RCEI will be used (Attachment 4).

C.	To minimize the possibility of a misunderstanding, each message should be acknowledged by the receiving station.  Acknowledgment should be made only after the receiving station completely understands the message.  A list of words commonly used for brevity, and their meaning, is included in Attachment 2.  The phonetic alphabet is shown in Attachment 3.

D.	Good judgment should be used when deciding which items are important enough to be passed on the nets, especially low in the count when nets are busiest.  However, if there is any doubt as to the importance of an item, it should be passed to the net controller for evaluation.

E.	Valuable net time can be saved if a few simple rules are followed:

1.	Have all the facts available when a trouble is reported.  Normally, time is saved if you get facts, evaluate the impact on support, and obtain an estimate on repairs before the trouble is reported.  An exception should be made low in the count, when troubles should be reported immediately and details should follow as soon as possible.

2.	Discussion of details can be more lengthy early in the count.  Only the more important troubles and readouts should be passed lower in the count.  Communications should be brief and factual.

3.	Short messages should be passed immediately following the preface without waiting for acknowledgment.  The preface of a longer message should include a brief statement of the message, such as "Operations - Tel-4, I have readouts."  This will aid the net controller in establishing message priority.

4.	Items and readouts of less importance which would not materially affect the progress of the operation should be held until requested or the net is not busy.

5.	It should be emphasized that for a busy net to be error free, each person passing a message on the net must be sure that the message is understood and acknowledged.

F.	Traffic should be crisp but not to the point where a repeat would be necessary.  Take care when passing information to be copied that the receiver has been given a moment to prepare for reception.  Remember, it is not possible to copy as fast as it is to read.

G.	From the time a net has been manned, no participant should leave the net unless released by net control.

H.	DO NOT - Conduct small talk on operational nets

-	Talk too fast

-	Interrupt transmission of higher priority

-	Use personal names

-	Use profane, indecent, or obscene language

-	Use unnecessary words (for example, ROGER that, that is AFFIRMATIVE, WAIT

ONE, I'll have to check

-	Use "CB" or "Ham" language

-	Request hold or scrub status gathered from unofficial sources

DO	-	Form what you want to say before you say it and have as much information

available as possible.

-	Be brief and accurate

-	Speak clearly and distinctly

-	Be patient and courteous

ATTACHMENT 1

COMMUNICATION NETS AND CONTROL STATIONS

Communication Net				Net Control Station

ATTACHMENT 2

PROWORDS

Proword				Explanation

Affirmative				Yes

Break					Separates the text from other portions of the message

Break Break				Interruption of traffic in progress for traffic of higher priority

Correction				There is a mistake in this transmission

FMC					Equipment is operational (Fully Mission Capable)

I read back				I am repeating your message as I copied it

I say again				I am repeating transmission or portion indicated

Negative				No

NMC					Equipment is not operational; cannot support the operation

as required (Not Mission Capable)

PMC					Equipment can support with a quick or partial repair (Partial

Mission Capable)

Roger					I have received your last transmission satisfactorily.  Do not

use in place of affirmative

Say again				Repeat all of the following part of your last transmission

Standby or Wait			Please wait a short time

That is correct				You are correct, or all that was transmitted is correct

Wilco					I have received your transmission, understand your instruc-

tions, and I will comply.

ATTACHMENT 3

PHONETIC ALPHABET

A - Alpha					N - November

B - Bravo					O - Oscar

C - Charlie					P - Papa

D - Delta					Q - Quebec

E - Echo					R - Romeo

F - Foxtrot					S - Sierra

G - Golf					T - Tango

H - Hotel					U - Uniform

I - India					V - Victor

J - Juliet					W - Whiskey

K - Kilo						X - X-ray

L - Lima					Y - Yankee

M - Mike					Z - Zulu

ATTACHMENT 4

ER FUNCTION STATIC CALL SIGNS AND MISSION IDENTIFIERS

Instrumentation			Static Call Sign**		Mission Identifier

ATTACHMENT 4

Instrumentation			Static Call Sign**		Mission Identifier

ATTACHMENT 4

Instrumentation			Static Call Sign**		Mission Identifier

Sub-units of particular stations/systems may use alphabetic designators "A" through "Z"

*  - 	Station/Site Number

ATTACHMENT 5

LAUNCH RANGE CONTROL