# SIMULATION OF THE FULL EMU ALIGNMENT SCHEME

The successful reconstruction of sensor locations in the prototype ISR system strongly suggests that the design of the EMU Alignment System is promising.  However, the ISR prototype system does not provide sufficient enough grounds to make larger generalizations about the entire EMU Alignment scheme nor characterize the interactions between many of the components.  A general simulation of the EMU alignment scheme is needed to evaluate the operational viability of the system as a whole, estimate the precision with which the system can reconstruct CSC chamber positions, and relate the contribution of uncertainties in the construction of individual components to the performance of the system as a whole.  Simulations of an idealized EMU system were performed with COCOA v2.0.0.  The simulations included all major system components and appropriate CSC chamber geometries.

## Construction and Extraction of Simulation Parameters and Objects

To optimize the development of Endcap simulations in COCOA, it was decided to compose the simulated Endcap solely from objects arranged in a ‘parent-child’ relationship.  This means that relatively simple collections of objects already defined in COCOA can be placed together to compose more complex objects.  In this scheme, two DCOPS sensors can be arranged in a local coordinate system to define a CSC chamber (Figure A.5).  Four CSC chambers, in turn, are arranged  to form a SLM line, three SLM lines are arranged to form an Muon Endcap (ME) layer, and six ME layers are assembled to form the entire CMS Endcap Muon system.  The modeling of components in this manner means that the location and orientation of all the individual components (dowel pins, chamber active reference centers, lasers, etc) does not need to be known in the general CMS coordinate system beforehand. Rather, the spatial relationships between parent and child objects can be specified directly from CMS production drawings.  This method works very well for six of the Muon Endcaps (ME(2, (3, and (4 Endcap), however the unique construction of the inner most Endcaps (ME (1) requires a somewhat less symmetric approach, as SLM lines do not traverse the ME discs and a Secondary Laser Line must be introduced.

The extraction of the information necessary to define these relationships from CMS production drawings involves several steps and is not a simple exercise of comparing two points in a single drawing.  For this reason, the exact manner in which parent-child objects were composed and assigned in the simulation is specified in Appendix A.  Components included in the simulation include inclinometers, DCOPS sensors, LINK 2D transparent sensors, crosshair and beam lasers, and distance measuring devices.  The objects created from these components include all the CSC chambers, transfer plates, and MABs used in the EMU alignment scheme.

The most important object in the simulation is the basic CSC chamber object.  Though the details of CSC construction in the simulation are found in Appendix A, the approach taken to describe the basic ME chamber object is shown in Figure 3.1.  Of principle importance is the manner in which the chamber ‘center’ is defined.  Since tolerances between the separation of strip layers is not controlled in CSC chamber production, it has been decided to define a ‘Reference Center’ (or ‘Active Centerpoint’) for the chambers as the average strip position projected onto the upper strip plane.  For a perfectly constructed CSC chamber (no uncertainties in construction), the centerline of the CSC chambers will fall along the Active Reference Center of the simulated chambers.  Note: the ‘Reference Center’ and ‘Active Centerpoint’ will be simply referred to as the ‘chamber center’ for the remainder of this discussion.

Figure 3.1: The Simulated CSC Chamber Geometry and Local Coordinate System in the Idealized COCOA Model.   The ‘Average Active Center’ of the CSC chambers is taken as the Reference Center for COCOA EMU simulations.

## Final Simulation Script Geometry Compared to Theoretical Placement

A complete model of the CMS EMU Alignment System constructed with the components detailed in Appendix A show layout and placement errors in the COCOA EMU simulation components of <5 (m along the Transfer Line (average deviation of  .05 (m) and 10 (m along the SLM Line (average deviation of  .81 (m).  The discrepancies on SLM on the order of 10 (m occur only on the placement the inner ME (2/1 DCOPS sensors relative to the ME (2/1 CSC chamber centers.  It has been decided that this error lies in the corresponding ME (2/1 production drawings.  The decision has been made to match components in the COCOA simulation to the final production drawings rather than a perfect CMS geometry.  It is expected that the tolerance on the construction of the components comprising the system will greatly exceed any of these small discrepancies in the production drawings.

A snapshot of a VRML model of the final simulation as generated by COCOA, showing only active components (lasers and all measurement devices), is shown in Figure 3.2.

Figure 3.2: The Simulated EMU Alignment System.   This is a COCOA generated VRML representation of the simulated geometry used for the idealized simulations of the EMU Alignment System.

## Estimation of Uncertainties Used in EMU Simulations

The primary goal of the COCOA simulation of the EMU alignment scheme is to obtain an estimate of the uncertainties associated with the reconstruction of CSC chamber positions along the SLM laser lines and an understanding of the relationships and correlations between the various components of the alignment system.  For simplicity, the most studies and simulations were done with the idealized EMU.  The idealized EMU system contains all the EMU system components arranged in the manner detailed in Appendix A with uncertainties on the location and placement of the components set to the estimations detailed below.  Since the system is ideal, it is assumed that all measurement devices are able to make a successful measurement and the full redundancy of the alignment scheme (multiple measurements of opposing lasers) is exploited.  The effects of component failure (missing CCDs measurements from DCOPS, faulty laser modules, inadequate resolutions) should be examined separately.

### Digital CCD Optical Position Sensor (DCOPS) Sensors

DCOPS sensors are viewed as a collection of four independent vectors, corresponding to the four CCD pixel arrays, referenced to a common calibration slot on the DCOPS hardware assembly (where the CSC calibration pin is to be inserted).  Systematic uncertainties in the location of the origin of these vectors, i.e. the first active pixel position, are generally independent of the uncertainties associated with the pixel array orientation.  Uncertainties in the location of any given pixel in a CCD to the calibration slot can be separated into uncertainties directly associated with the calibration of the first pixel position and those associated with the pixel array orientation and length.

#### Uncertainties in Direct Calibration of First Pixel Position

Calibration of first active pixel positions to the reference pins for large numbers of sensors is done on a specially designed test bench at Northeastern University (NEU).  The calibration bench is constructed of a laser diode assembly, a single directional DCOPS sensor that has been previously calibrated under a microscope, and a mount for the DCOPS sensor that is to be calibrated.  In this arrangement, the calibrated DCOPS sensor acts as a mask to calibrate the uncalibrated DCOPS sensor.  NEU indicates typical uncertainties in the first pixel location using this calibration technique will not exceed 40 (m [3.1].

#### Uncertainties in Pixel Array Orientation and Length

For simulation and reconstruction purposes, it is assumed that the four CCD vectors lie in the local DCOPS XY reference plane and run parallel to the X or Y axis.  The error introduced by this assumption manifests itself as a correction to the Sony specified pixel-to-displacement conversion of 14(m per pixel along the array.  The uncertainty in the determination of the position of the charge distribution will scale across the pixel array as the cosine of the angle by which the CCD array deviates from its optimal orientation.

The uncertainty introduced by the error in pixel array length and the misorientation of the pixel arrays can be estimated as the quadrature of the maximal error due to the misalignment of the pixel arrays within the CCD packages, the uncertainty in the length of the pixel array, and the maximal error due to misalignment of the CCD package within the DCOPS window frame.

#### Uncertainty of CCD Array and Packaging Positioning

Direct measurement of the pixel array length was performed on a representative sample of ILX-551 CCDs.  In addition to the 2048 active pixels in each pixel array, one end of the array contains an additional 33 dummy pixels while the other end contains an additional 6 dummy pixels.  The total length of the pixel strip is calculated to be 29.218 mm based on the Sony pixel specification of 14 x 14 µm2 with no manufacturer quote on the uncertainty in pixel size.

Sony has provided estimates of uncertainties for the placement of the first pixel in the array in the CCD package, but does not offer any estimate as to the uncertainty in the pixel array length or orientation.  These uncertainties where estimated as the maximal deviation from Sony specifications found in the small set of CCDs studied.  Systematic errors embedded in the ILX551A CCD packages have been studied on a small sample of unmounted CCDs.  Direct measurements of the pixel array lengths on these samples revealed a maximum discrepancy of (50 ( 10) µm with the Sony specification [3.1].  All measurements of the array lengths yielded a result which was always greater than the Sony specified value.

Uncertainty occurring in the final active pixel position as the result of a misalignment of the pixel array within the CCD package has been determined to be less than 4 (m based on a measured 15 mrad deviation of the array with the package edge (maximum misorientation found in the small sample of measured CCDs) [3.1].

Figure 3.3:   SONY ILX-551 CCD Specification and Direct Measurement (mm).  The dimensional specifications and tolerances for the ILX-551 (A) quoted from Sony and the dimensions of a CCD taken from the small sample of studied ILX-551s (B) which exhibit the greatest deviation of the pixel array (in red) placement from the optimal location.

#### Uncertainty of CCD Package Orientation inside DCOPS Window Frame

Uncertainty occurring in the final active pixel position as the result of the misalignment of the CCD package, and thus the encased pixel array, scales as the cosine of misalignment.  The present DCOPS window frame design incorporates a specially designed polycarbonate mount for the CCDs.  Tolerances for the positioning of each end of the 53.71 mm long CCD mounts in the window frame is (100 µm, contributing an error of less than 1 µm in the determination of the distance along the pixel array.  Tolerances for the placement (orientation) of the CCDs within the polycarbonate mounts are estimated at >20 mrad, contributing a maximal uncertainty of less than 10 µm in the determination of the last active pixel in the array.

#### Final Estimation of Uncertainty in CCD Pixel - DCOPS Reference Pin Calibration

The final estimation of the uncertainty associated with the determination of the location of any given pixel in the DCOPS sensor relative to the CSC reference slot is taken to be the quadrature of all known errors in the determination of the first and last active pixel positions in the pixel array.  In addition to the systematic errors associated with the placement of CCD arrays relative to the primary reference pin, the manner and stability in which the centroid of charge distributions are determined must be considered.  It has been determined from the 2000 ISR Tests that centroids from successive measurements on the CCD are repeatable to (14 µm.  This uncertainty is characterized as the uncertainty associated with a particular measurement and considered separately in the COCOA simulation.  The contributions and final estimate of the systematic uncertainty associated with the placement of pixels is given in Table 3.1.

Table 3.1:  Contributions to Final Error in Determination of Pixel-to-CSC Reference Pin Calibration.   Uncertainties due to misalignment and pixel array length are estimated as the worst case errors in the determination of the final active pixel position.

| Uncertainty Origin | Magnitude (µm) |
| --- | --- |
| Direct Calibration of First Pixel (NEU Estimate) | 40 |
| Array Misalignment (inside package) | 4 |
| Array Length | 50 |
| Package Misalignment | 10 |

### CSC Active Center - DCOPS Reference Pin Calibration

As previously discussed, Cathode Strip Chambers are described in terms of their ‘active center’, which corresponds to the average of the individual panel active areas projected onto the plane of the first panel (See Appendix A for more detail on chamber definition).  Determining the certainty with which this active center can be externally referenced is crucial to the successful simulation and reconstruction of the Endcap Muon System.  Uncertainties in the determination of the relationship between CSC active cathode strips and DCOPS reference pins can be separated into uncertainties associated with individual panel definitions and manufacture, assembly of multiple panels to form the complete CSC chamber, the mounting assemblies which affix the DCOPS sensors to the surface of the assembled chamber, and deformations in the chamber after installation in CMS.

All estimations of uncertainties addressed here regarding CSC chamber and DCOPS mounting hardware tolerances are typically gathered from the specified tolerances placed on the fabrication of components.  In most cases, particularly CSC panel definitions, adherence to these tolerances has been confirmed by direct measurement on an appropriate number of preproduction samples.  However, there are many components which have not yet been produced on a large scale.  Uncertainties for these components have been estimated from production drawings.  A far more meaningful estimation of uncertainties for such components should be taken from the rms value of deviations found from a sufficient sample of the finished products.

In keeping with the convention established in Appendix A, the local chamber coordinate system is taken as right handed with the local Z axis running across the chamber centerline from the narrow end of the chamber to the wider end and the local Y axis running from the bottom layer to the top layer of cathode strips.

#### CSC Panel Definition

All cathode strip chambers are constructed of a polycarbonate honeycomb panels with 1.5 mm G-10 epoxy fiberglass skins coated with a 34 (m layer of copper.  Individual panels are first drilled with two CSC Alignment Holes (where the CSC Alignment Pin will ultimately be inserted) along the centerline (See Figure 3.4).  These two holes ((25 (m tolerance on the diameters) establish the reference system from which all other machining on the panel is established.  A high precision router is then used to mill the cathode strips and associated artwork directly into the copper surface of the panel.  Accuracy of the router has been confirmed by direct measurement.  Errors in absolute strip position exhibit accumulative systematics over chamber width due to the manner in which they are milled.  Quality control measurements on more than 300 panels have shown a ((average active area) of 25 (m and rotational uncertainty of 7 (rad.  However, measurements of the total active area across the widest end of these panels show a ((width) of 40 (m whereas the same measurement across the narrow end of the panel reveals a ((width) of 113 (m.  Since the straightness strips have been measured as having a ((rms) < 22 (m, the effect is likely due to the fact that the strips are milled into the panel in only one direction (from the wide end to narrow end).

Figure 3.4:  Placement of Pins, Holes, and Etchings on CSC Chamber [3.2].

Additionally, a series of ten slot cuts are placed on each panel for future calibration and quality control as well.  The slot cuts are referenced directly to the center line defined by the two CSC Alignment Holes as well as a particular cathode strip number -- but not necessarily the first strip nor the same strip in all chambers.  Each mark is referenced within (25 (m to the center point of the CSC Alignment Holes and within (25 (m to the particular strip being referenced (the “Reference Strip”).

A series of secondary dowel pins and slots used to mount the DCOPS sensors to the chamber surface are also drilled at this time.  On the wider end of the chamber, these holes position the precision pins and bolts used by the DCOPS mounting brackets to reference the CCDs directly to the cathode strips.  On the narrow end, a series of holes for alignment pins are established which locate the plates for DCOPS mounting hardware to be glued to the panel surface.  The locations of all holes are placed with a certainty of (25 (m on the surface of each panel and have their diameters drilled to a certainty of (25 (m.

#### Assembly of Final Chamber from Multiple Panels

Once all six panels are milled and prepared, they are layered to form the composite six layer CSC chamber.   The precision with which each panel in the chamber is positioned with respect to neighboring panels can be estimated from the uncertainty with which the central CSC Alignment Holes are placed ((25 (m) and the tolerance placed on the diameter of the hole itself.  Since the placement of all six layers are independent of each other, the maximal misalignment of any two given planes (two sets of holes, each with  25(m uncertainty in the diameter and relative location of  their center points) is estimated to be (50 (m.  The uncertainty in the average center point across all six chamber planes is (87 (m.

After the panels are stacked together, a frame is mounted to the edges of the chamber to add rigidity to the structure, protect connections, and form a Faraday shield around the electronics.  Though the DCOPS mounting tower assemblies will mount on top of the frame structure, placement of the tower mounting hardware is completely determined by an alignment pin that sits in the previously drilled alignment holes.  Since the CMS triggering requirements will accommodate relatively large uncertainties in the final determination of the chambers along the CMS Z coordinate, the placement of elements along the local Y axis of the chamber (CMS Z), including the frame, is not tightly controlled during manufacturing.  The certainty with which the placement of the frame above the first strip plane will be known is estimated to be (127 (m.  The frame itself is estimated as being flat to (25 (m whereas chamber flatness is estimated as no worse than (200 (m across any 60 cm span.  Tolerances on the panel thickness are asymmetric, +508 (m to -254 (m, and determined by the manner in which the panels are manufactured and cut.

#### Alignment Mounting Hardware

Mounting hardware to attach the DCOPS sensors to the chamber frames is similar across all chamber varieties.  The mounting hardware consists of a series of spacers, shims, and mounting plates which secure the primary DCOPS mounting bar (where CCD-dowel calibration is done).  CSC chambers in both inner and outer rings of ME (2, (3, and (4 disks are placed into two layers.  The chamber configuration for Trigger towers makes it necessary to mount hardware on the back layer for one outer CSC.  Chambers on back layers will have mounting hardware called towers to give the attached DCOPS sensor an elevation in the SLM line which matches the front layer.

As previously noted, sensors affixed to the larger end of the chambers (+Z local end) are mounted directly to the chamber frame while sensors on the smaller end of the chamber (-Z local end) are attached to a special plate which is glued into position with the aid of a special pin and slot set during the fabrication of the chamber.  The precision with which the inner plate can be glued to the surface of the chamber is determined from the tolerance with which the pin and slot are placed on the chamber surface (( 25 (m each) as well as the precision with which the receiving pin and slot are placed on the plate to be glued (( 25 (m each).  Therefore, it is estimated that the DCOPS plates on the narrow end of the chamber can be glued in position within (50 (m of the specified location - approximately the same tolerance with which they can be attached on the +Z local end to the chamber frame.

Although the heights of the towers on the back layers differ by 290 mm from the standard brackets, the plates and assemblies used are essentially the same.  The mounting brackets are attached across two standoffs, each with an asymmetric tolerance of +.100 -0.000 mm.  The standoffs locate a set of dowel pins on a stock Aluminum jig plate (( 125 (m thickness).  The DCOPS mounting bar connects directly to this plate.  Holes and pins used to secure the DCOPS are positioned and drilled to (25(m, contributing an additional (50 (m uncertainty in the referencing of the sensors to the strip positions.

The potential uncertainty in the orientation of the DCOPS sensors about the primary DCOPS dowel pin due to the uncertainty of the standoffs (separation of 88mm) is less than (1(rad.  Likewise, the uncertainties of the chamber frame positioning above the first panel on the chamber contribute an angular uncertainty about the same axis of less than (1(rad as well.  Rotational uncertainties about other axes are found to be only slightly larger, but can be safely neglected by COCOA as each CCD is one dimensional.

#### Deformation of Chambers and Chamber Components

One final consideration in defining the precision with which individual layers can be externally referenced is the deformation of the chambers when mounted in the detector.  Since the CSC chambers are mounted vertically, the weight of the chambers creates a shearing effect across the six layers of the chamber.  This effect is will be most prevalent when the shearing occurs perpendicular to the direction of the cathode strips.  Thus, the effect is largest for chambers lying along the CMS X axis.  The displacement of the individual layers due to the shearing force increases from the bottom layer (closest to the RF iron mounts) to the top layer.  The maximal displacement of the uppermost layer has been directly measured as less than 25 (m.

#### Angular/Rotational Uncertainties

Components in COCOA are specified by their location and orientation making it necessary to estimate the rotational uncertainties with which the DCOPS sensors are placed on the chamber.  Since the CCDs used in the DCOPS sensors are one dimensional pixel arrays, rotational uncertainties about the axis normal to the plane of the CCDs (DCOPS local Z axis) are the most important.  Estimations of uncertainties about this axis, where it might be expected the slope and flatness of surfaces will contribute most, can also be estimated from the tolerance and separation on the mounting bracket standoffs, CSC panel/frame uncertainty (127(m), length (>>100cm), and flatness ((200 (m across 60 cm), and other tolerances placed on the components in the mounting bracket (Al plate, DCOPS window mounting bar - both (25-50(m across (90mm). The uncertainties about the DCOPS Z axis are summarized in Table 3.3.

Uncertainties about the DCOPS X and Y axis are determined from the uncertainties of the two precision pins or holes used to position components on the chamber and mounting brackets and the separation between them.  In all cases, the uncertainties associated with the placement of pins and holes ((25-50(m) and the relatively large span of between them ((90mm) mean individual contributions to the rotational uncertainty in the orientation of the DCOPS sensors is on the order of 1 (rad.  The uncertainties about the DCOPS X and Y axes are summarized in Table 3.2.

#### Final Estimation of DCOPS - CSC Active Center Uncertainties

The final uncertainty associated with the DCOPS reference pin - CSC active centers is determined from the quadrature of all estimated uncertainties in the plane of the strips (Table 3.3) and perpendicular to the plane of the strips (Table 3.2). The estimated rotational uncertainties about the DCOPS X, Y, and Z axes are summarized in Table 3.4 (DCOPS Z axis) and Table 3.5 (DCOPS X and Y axes).  The rotational uncertainties have been estimated from the uncertainty and separation of the pins and/or holes which join components.

Table 3.2:  Estimation of Error of DCOPS Positioning Above First Strip Layer (local Y axis).  This table shows the uncertainties associated with the determination of the displacement between the DCOPS mounting plate and the first plane of cathode strips.

| Uncertainty Origin | Magnitude (µm) |
| --- | --- |
| Panel Thickness (Maximal deviation) | 508 |
| Frame to Panel Placement | 127 |
| Mounting Bracket Chamber-Shim Standoff | 100 |
| Mounting Bracket Al. Plate | 125 |
| Final Estimation of Uncertainty in Y Plane of Chamber | 548 µm |

Table 3.3:  Estimation of Error Transverse to CSC Chamber Centerline.  This table shows the uncertainties associated with the determination of the displacement between the DCOPS alignment pin and the cathode strips transverse to the chamber centerline (local chamber X axis).

| Uncertainty Origin | Magnitude (µm) |
| --- | --- |
| Central Alignment Pin - Notched Alignment Marks | 25 |
| Notched Alignment Mark - Numbered Reference Strip | 25 |
| Intrinsic Strip Positioning (from milling) | 30 |
| Averaged Centerline Across 6 Assembled Planes | 87 |
| Positioning of Primary DCOPS Alignment Pins/Holes | 25 |
| Diameter of Primary DCOPS Alignment Pins/Holes | 25 |
| Placement of Mounting Plate On Chamber | 50 |
| Placement of DCOPS Mounting Plate | 50 |
| Maximal Shearing Effect | 25 |
| Final Estimation of Uncertainty Along X Axis of Chamber | 129 µm |

Table 3.4:  Estimation of Error of DCOPS Orientation About DCOPS CCD Plane Normal (local DCOPS Z axis).  This table shows the uncertainties associated with the determination of the orientation between the DCOPS CCDs and the first plane of cathode strips.  Most uncertainties were less than 1 µrad and have been rounded up.

| Uncertainty Origin | Magnitude (µrad) |
| --- | --- |
| Upper Cathode Panel - Frame Relationship | 1 |
| Frame (or Fwd Glue Plate) - DCOPS Mounting Bracket Base | 1 |
| DCOPS Mounting Bracket Base - Mounting Bracket Shim Plate | 1 |
| Mounting Bracket Shim Plate - DCOPS Mount Bar | 1 |
| Straightness of DCOPS Mount Bar - DCOPS Window Frame | 1 |
| Total Uncertainty in DCOPS Orientation on Chamber | 2.2 µrad |

Table 3.5:  Estimation of Error of DCOPS Orientation of DCOPS CCD Plane (local DCOPS X/Y axis).  This table shows the uncertainties associated with the determination of the orientation between the DCOPS CCDs and the first plane of cathode strips.  Most uncertainties were less than 1 µrad and have been rounded up.

| Uncertainty Origin | Magnitude (µrad) |
| --- | --- |
| Upper Cathode Panel Pins/Holes | 1 |
| DCOPS Mounting Bracket Base | 1 |
| Mounting Bracket Shim Plate | 1 |
| DCOPS Mount Bar | 1 |
| Total Uncertainty in DCOPS Orientation on Chamber | 2 µrad |

### Estimation of Other Simulation Parameters and Uncertainties

The complete simulation of the EMU alignment scheme includes several components in the Link Alignments system.  Link components found in the COCOA EMU simulations include the MABs, Secondary Link lines, and  the ME ±1/2 ‘ALMY’ sensors.   The uncertainties in the construction and/or performance of these components have been taken from a COCOA simulation of a quarter Link plane [3.3] and discussions [3.4] with the Link Alignment group.   A summary of the uncertainties assigned to these components in the simulation is given in Table 3.6.

Table 3.6:  Estimation of LINK System Uncertainties.  This table shows the estimated uncertainties associated with components in the Link Alignment System included in the EMU Idealized COCOA Simulation

| Uncertainty Origin | Magnitude |
| --- | --- |
| LINK Reconstructed MAB Position | 135 µm |
| LINK Reconstructed MAB Orientation | 10 µrad |
| DCOPS Location within MAB | 50 µm |
| DCOPS Orientation within MAB | 2 µrad |
| Definition of Secondary Link Line | 10 µm, 2 µrad |
| ME ±1/2 ALMY Sensor Resolution | 5 µm |

## Simulation Results (Idealized EMU System)

The primary goal of the COCOA simulation of the EMU alignment scheme is to obtain an estimate of the uncertainties associated with the reconstruction of CSC chamber positions along the SLM laser lines and an understanding of the relationships and correlations between the various components of the alignment system.  For simplicity, most studies and simulations were done with the idealized EMU.  The idealized EMU system contains all the EMU system components arranged in the manner detailed in Appendix A with uncertainties on the location and placement of the components set to the estimations previously discussed.  Since the system is ideal, it is assumed that all measurement devices are able to make a successful measurement and the full redundancy of the alignment scheme (multiple measurements of opposing lasers) is exploited.  The effects of component failure (missing CCDs measurements from DCOPS, faulty laser modules, inadequate resolutions) are examined separately.

The layout of CSC chambers, transfer plates, and SLM lines exhibit a high degree of symmetry between ME layers on YE Iron discs.  The symmetry of most components is reflective between discs, which is to say chambers on ME+2 appear mirror symmetric to chambers on ME-2.  This is not generally true for DCOPS sensors located on the transfer plates.  The placement of DCOPS sensors into the transfer plate design for each ME disc was based on the ensuring that the pointing (i.e. the normal to the CCD plane) of the DCOPS sensors was consistent for all layers, the orientations of otherwise symmetric DCOPS sensors were rotated 180º about the local Y axis of the calibrated dowel pin. This effectively changes the distance between several of the transfer plate SLM DCOPS dowel pins and transfer plate Transfer Line DCOPS dowel pins.  Additionally, the transfer plates located at Point 5 on the ME layers must be elongated to avoid possible conflict with the YE Iron supports.  The extension of the distance between the calibrated dowel pins results in a leveraging of the uncertainties in the definition of the SLM laser and, ultimately, slight discrepancies in the spatial uncertainties between otherwise symmetric CSC chambers.  This effect is seen across all eight ME discs.  For this reason, simulation results presented here will deal with the average of all SLM chamber uncertainties for a particular coordinate in a chamber ring, or the specification of a small range of chamber uncertainties for a set of objects or chambers in a single ME disc.

The software was also found to put an enormous drain on the available computer memory.  The full EMU simulation of ME ±1, ±2, ±3 and ±4 Endcap Alignment System contained approximately 6200 separate objects to fit with at least 4700 non-zero correlations and was simply too large for the software to compute without exhausting its memory allocation.  Though a memory leak was identified (but could not be traced) when running the code, the sheer number of parameters  to compute requires a large amount of memory.  Since each element in the matrix requires eight bytes of memory (double precision) and there are at least 9,000,000 elements in each matrix (≈ 6000 x 1500) for the full simulation, at least 72 MB of memory are required for each matrix constructed.  As Section 2.1 indicates, at least seven unique matrices are required for a COCOA fit (> .5 GB). However since the fitting process requires an iterative update of matrices, the actual amount of memory required for a complete COCOA simulation of the EMU System  can quickly exceed 1 GB of memory after several iterations.  It was found that the largest simulation which could be successfully fit with the available computing resources (1 GB of memory) contained the ME ±2, ±3, and ±4 layer alignment systems.

### Comparison of Large Simulations vs. Small Simulations

Using the full COCOA simulation model, several attempts were made to obtain a fit of the complete 8 ME disc system.  These attempts failed with the computers reporting abnormal utilization and allocation of memory.  Indeed, when the memory usage of the system was examined, it was found that a serious memory leak was present. The memory leak was not so serious as to preclude the fitting of smaller subsets of the full EMU simulation model.  The largest simulation successfully fit consisted of the ME ±2, ±3, ±4 discs and transfer line system.  Fifty-three smaller subsets of the ME ±2, ±3, ±4 discs and transfer line simulation were also completed and compared amongst themselves and the larger 6 ME disc simulations.  These subsets included all possible permutations of systems composed of at least two ME discs with full transfer line systems (i.e. all simulations had the same number of transfer plates in the system).

Comparisons made between systems within the 53 subsets of two ME disc systems showed very little variation (< 10%) between the certainties with which identical chambers could be reconstructed.  Comparisons made between these two ME disc systems and the larger six ME disc system also yielded very little variation (< 5%) between the certainty with which identical chambers could be reconstructed.  This seems to confirm that there is very little coupling of components across different ME discs.

### Simulation of the Idealized System

The uncertainty in location for CSC chambers located along a particular SLM line may vary from the uncertainty of similar chambers located in other SLM lines.  The discrepancies between chamber uncertainties in ME discs with a similar SLM arrangement of components is expected to be small (<10µm).  For chambers in the same Endcap layer, this is primarily due to variations in the separation (i.e. lever arm) between transfer line and reference sensors placed on transfer plates located at the SLM endpoints.  Chambers located on different ME discs are affected by the manner in which the SLM laser line crosses the chamber and/or the compounding of errors to inner ME chambers.  Since SLM lines on ME ±1 discs are constructed in a very different manner from those on SLM ME ±2, ±3, and ±4 discs, more substantial variations are expected between chamber uncertainties when comparisons are made to ME ±1 chambers.  The mean uncertainty with which chamber locations and orientations along the SLM lines can be reconstructed in the EMU alignment scheme is summarized in Table 3.7 and Table 3.8.  The average deviations presented alongside the estimates represent the average deviation from the mean uncertainty determined for the all chambers located along a particular ME ring.

Table 3.7: Uncertainty in CSC locations along the SLM lines for the Idealized EMU System.  The uncertainty estimates for chambers in ME ±1/2 layer have been done using two sets of resolutions for the inclinometers placed on the ME ±1/2 CSC chamber frames

| CSC Chamber | Mean Uncertainty in Chamber Locations | Average Deviation of Uncertainty |
| --- | --- | --- |
|  | CMS R( (µm) | CMS Z (µm) | CMS R( (µm) | CMS Z (µm) |
| ME±1/2 (no inclinometer) | 515 | 717 | 17 | 9 |
| ME±1/2 (( inclinometer = short term ISR () | 90 | 385 | 2 | 5 |
| ME±1/2 (( inclinometer = long term ISR () | 187 | 415 | 2 | 1 |
| ME±1/3 | 216 | 878 | 3 | 22 |
| ME±2/1 | 205 | 467 | 10 | 12 |
| ME±2/2 | 221 | 509 | 7 | 24 |
| ME±3/1 | 230 | 491 | 14 | 15 |
| ME±3/2 | 248 | 520 | 20 | 22 |
| ME±4/1 | 241 | 525 | 14 | 17 |
| ME±4/2 | 259 | 524 | 20 | 17 |

Table 3.8: Uncertainty in CSC Orientations About Axes Parallel to CMS Coordinate System and Through CSC Chamber Center Idealized EMU System.  The uncertainty estimates for chambers in ME ±1/2 layer have been done using two sets of resolutions for the inclinometers placed on the ME ±1/2 CSC chamber frames.

| CSC Chamber | Mean Uncertainty in Chamber Orientation | Average Deviation of Uncertainty |
| --- | --- | --- |
|  | CMS R( (µrad) | CMS Z (µrad) | CMS R( (µrad) | CMS Z (µrad) |
| ME±1/2 (inclinometer short term ISR () | 95 | 95 | N/A | N/A |
| ME±1/2 (inclinometer long term ISR () | 698 | 698 | N/A | N/A |
| ME±1/3 | 138 | 1168 | 3 | 360 |
| ME±2/1 | 113 | 812 | 0 | 252 |
| ME±2/2 | 74 | 771 | 0 | 297 |
| ME±3/1 | 834 | 888 | 244 | 261 |
| ME±3/2 | 742 | 777 | 303 | 323 |
| ME±4/1 | 725 | 909 | 383 | 241 |
| ME±4/2 | 1105 | 839 | 126 | 315 |

In addition to variations in chamber reconstruction uncertainties between different SLM lines and ME discs, chamber reconstruction uncertainties within a particular SLM line may vary.  This is expected since the spacing of DCOPS sensors is not the same for chambers on the inner and outer rings of the discs.  Chambers of the same type and on the same SLM line are expected to have similar uncertainties.

The original ME ±1 alignment scheme did not incorporate inclinometers on ME ±1/2 chambers. It had been assumed that the ME ±1/3 SLM lines, having been offset from the Secondary Link laser lines, would provide sufficient angular definition about the local chamber Z axis for the ME ±1/2 chambers (sensors on these chambers cannot discern rotations about the laser lines).  Simulations of the ME ±1 layer (results shown in Table 3.9 and Table 3.10without inclinometers revealed poor spatial and rotational resolution on all ME ±1 chambers and did not meet the estimated system performance.  For this reason, inclinometers similar to those employed on the transfer plates were incorporated into the ME ±1/2 chamber frames.  Simulations of the idealized system are performed with the resolution of these inclinometers set to be equivalent to the long term resolution of the inclinometers studied during the 2000 ISR tests.

Table 3.9: Uncertainty in ME ±1 CSC locations along the SLM lines for the Idealized EMU System without ME ±1/2 Inclinometers. The uncertainty estimates where prepared in an Idealized EMU ME±1 simulation.

| CSC Chamber | Mean Uncertainty in Chamber Locations | Average Deviation of Uncertainty |
| --- | --- | --- |
|  | CMS R( (µm) | CMS Z (µm) | CMS R( (µm) | CMS Z (µm) |
| ME±1/2 (no inclinometer) | 515 | 717 | 17 | 9 |
| ME±1/3 (no inclinometer) | 291 | 965 | 5 | 111 |

Table 3.10: Uncertainty of ME ±1 CSC Orientations About Axes Parallel to CMS Coordinate System and Through CSC Chamber Center for Idealized EMU System without ME ±1/2 Inclinometers.  The uncertainty estimates where prepared in an Idealized EMU ME±1 simulation.

| CSC Chamber | Mean Uncertainty in Chamber Orientation | Average Deviation of Uncertainty |
| --- | --- | --- |
|  | CMS R( (µrad) | CMS Z (µrad) | CMS R( (µrad) | CMS Z (µrad) |
| ME±1/2 (no inclinometer) | 1517 | 1521 | 553 | 538 |
| ME±1/3 (no inclinometer) | 1331 | 1333 | 425 | 460 |

### Relationships and Correlations Between EMU Components

Since COCOA calculations are based on variance-covariance matrix operations, the final matrix returned from the fitting process contains additional information concerning the relationship between reconstructed quantities in the simulated system. However, relationships between most components must be inferred by a series of simulations, with small variations in each simulation.

A large number of such simulations were conducted to explore the relationship between the largest sources of uncertainties within the EMU alignment scheme and several key components of the system.  In general (details to follow), the uncertainties ascribed to system components in Section 3.3.2.6 were varied in a systematic manner to gauge their impact on the determination of CSC chamber positions.  This information is particularly important during the design and pre-production stages of the EMU project, as the cost of manufacturing and materials is highly dependent upon the tolerances placed on the components and equipment being employed.  It is also instrumental in validating the operational viability of the EMU alignment scheme.  Since the EMU Alignment scheme will be staged with an initial deployment of ME (1 and ME (2 layer systems, the focus of these studies has been directed toward these ME layers.

#### Correlations Between ‘Unknown’ Quantities

The correlations between unknown entries in the simulation are given by the off-diagonal elements of the variance-covariance matrix returned by the COCOA fit.  CSC chambers in the simulation typically showed hundreds of correlations with other components, however only a few correlations exceed .01 (1%).  A typical sample of the most significant correlations between the five unknown chamber parameters (2 spatial, 3 rotational) and other unknown simulation parameters is shown in Table 3.11.  The correlations given in Table 3.11 are representative of most CSC chambers in the simulation: the most significant correlations between unknown parameters were generally confined within SLM lines and connecting transfer lines.

Looking at a sample of the correlations between various transfer plates in Table 3.12, it is evident most correlations are less than 15%. The largest correlations exist between transfer plates located along the same Transfer laser line (see Appendix A, Section 5.2.6, for labeling scheme).  The coupling of individual Transfer Laser Lines across SLM lines (i.e. opposing Transfer Lines) was expected to be weak since the transfer line MAB reference points are relatively well known and the six indirect interactions between the three pairs of opposing Transfer Laser Lines are connected only by initially undefined SLM laser lines.  Since correlations between transfer plates are weak, and correlations between transfer plates and chamber along the same SLM lines are always less than 1, correlations between CSC chambers which do not fall along the same SLM laser lines are weak (< 5%).

Table 3.11: Sample Correlations between Reconstructed Entries for CSC Chamber ME–22_15 (SLM-23).  The correlation between entries shown in the table is taken directly from the off-diagonal matrix elements of the variance-covariance matrix used in the COCOA fit.  This sample (it is not complete) of entries represents the largest correlations found for this chamber and was prepared from an ME (1 and ME (2 simulation.  Entries are taken to be in the local coordinate system of the objects they describe (Appendix A).

| ME-22_15 Parameter | Dependent Object | Correlation |
| --- | --- | --- |
| Centre_Y | slm-23/me-22_32_angles_Z | 0.143 |
| Centre_Y | slm-23/me-21_8_centre_Y | 0.136 |
| Centre_Y | transfer1_angles_X | 0.081 |
| Centre_Y | slm-23/me-21_8_centre_Y | 0.059 |
| Centre_Z | slm-23/me-22_15_angles_X | 0.769 |
| Centre_Z | transfer1_angles_Z | 0.326 |
| Centre_Z | slm-23/me-21_8_angles_X | 0.326 |
| Centre_Z | slm-23/me-22_32_angles_Y | 0.294 |
| Centre_Z | slm-23/me-22_15_angles_Z | 0.273 |
| Centre_Z | transfer-1_angles_X | 0.017 |
| Angles_X | transfer-1_angles_X | 0.457 |
| Angles_X | slm-23/me-22_32_angles_Y | 0.279 |
| Angles_X | transfer1_angles_Z | 0.265 |
| Angles_X | slm-23/me-21_8_angles_X | 0.265 |
| Angles_X | slm-23/me-22_15_angles_Z | 0.187 |
| Angles_Y | transfer-1_centre_Y | 0.651 |
| Angles_Y | transfer1_angles_Z | 0.183 |
| Angles_Y | transfer1_angles_X | 0.183 |
| Angles_Y | transfer-1_angles_Y | 0.040 |
| Angles_Z | slm-23/me-21_8_centre_Y | 0.618 |
| Angles_Z | slm-23/me-22_32_angles_Y | 0.177 |
| Angles_Z | slm-23/me-21_8_angles_X | 0.111 |
| Angles_Z | transfer1_angles_Z | 0.111 |
| Angles_Z | transfer-1_angles_X | 0.017 |

Table 3.12: Sample Correlations between Reconstructed Entries for Transfer Plate. The correlation between entries shown in the table is taken directly from the off-diagonal matrix elements of the variance-covariance matrix used in the COCOA fit.  This sample (it is not complete) of entries represents the several non-zero correlations found between transfer plates in an ME (2, (3, (4 simulation.  Transfer plates labeling has all objects designated as ‘transfer_plateAB’, where two plates with the same value of  ‘B’ lay on the same Transfer laser line (see Appendix A, Section 5.2.6)

| Object 1 | Object 2 | Correlation |
| --- | --- | --- |
| transfer_plate21_centre_X | transfer_plate24_centre_Z | 0.03 |
| transfer_plate-21_centre_X | transfer_plate-31_centre_X | 0.10 |
| transfer_plate-21_centre_Z | transfer_plate-31_centre_Z | 0.10 |
| transfer_plate24_centre_Z | transfer_plate26_centre_Y | 0.02 |
| transfer_plate24_centre_Z | transfer_plate34_centre_Z | 0.14 |
| transfer_plate24_centre_Z | transfer_plate36_centre_Z | 0.03 |
| transfer_plate22_centre_Z | transfer_plate32_centre_Z | 0.14 |
| transfer_plate26_centre_Y | transfer_plate36_centre_Z | 0.09 |
| transfer_plate34_centre_Z | transfer_plate36_centre_Z | 0.08 |
| transfer_plate-32_centre_X | transfer_plate-42_centre_X | 0.02 |
| transfer_plate44_centre_X | transfer_plate-31_centre_Z | 0.01 |
| transfer_plate44_centre_X | transfer_plate-21_centre_Z | 0.01 |

#### Correlations Between ‘Known’ and ‘Unknown’ Quantities

Correlations between the uncertainties in the construction of components within the simulation and the certainty with which chambers can be reconstructed provides valuable information for the design of these components being studied.  The goal of exploring the relationships between the design of EMU components and the performance of the system is to maximize system performance while minimizing costs.  Particular attention was paid to chambers in the ME (1 and (2 layers, as muons traversing these layers experience a much greater magnetic field, and thus a larger sagita, than in the ME (3 and (4 layers.

In general, these studies examined the dependence of chamber spatial CMS RPhi uncertainties versus the resolution or tolerances of a particular component.  Simulations were done with two opposing ME layers (i.e. ME (1 or (2), a full Transfer Line system, inclusion of inclinometers on ME (1/2 (resolutions set at long term ISR values), and in a manner otherwise consistent with the simulations used to produce Table 3.7 and Table 3.8 unless specified.

#### LINK Interface to EMU Alignment System

The interface of the EMU alignment scheme to the Link alignment scheme provides Tracker coordinate information to the MABs and Secondary Link lines.  The certainty with which MAB and Secondary Link lines are defined directly impacts the precision with which chambers centers can be reconstructed.  Uncertainties in the Link interface fall into three categories: uncertainties in the construction of the MABs, uncertainty in the definition of the Secondary Link lines, and uncertainties in the rhomboid prism which split the Primary and Secondary Link Lines.  Uncertainties in the rhomboid prism can also be regarded as any other potential uncertainty which propagate to both the MABs and Secondary Link lines.

The estimated uncertainty in MABs position and orientation is given in Section 3.3.3.  This estimated includes allowances for distortions in the MAB as well as the placement of a DCOPS sensors within the structure. Figure 3.5 shows how the uncertainty in reconstructed CMS RPhi chamber positions in ME (1 and (2 varies as a function of the uncertainty on the MABs.

Since ME (1 chambers are reconstructed in part by the Secondary Link line, the dependence on Transfer Laser lines (and thus the MABs) is relatively weak.  This is particularly true for the ME (1/2 chambers, where there is no dependence on the MABs for spatial reconstruction in CMS RPhi.  The short lever arm between the ME (1 (outer) Transfer Plates and placement of the ME (1/3 SLM reference sensor on the ME (1/2 chamber frame dampens the interaction between the MABs and ME (1/3 chamber reconstruction as well.

ME (2 chambers (as well as ME (3 and ME (4 chambers) must be reconstructed solely from the MABs.  As a result, a strong coupling between the uncertainties on the MABs and reconstructed chamber locations is seen.

Figure 3.5:  Reconstructed CSC RPhi Chamber Uncertainty vs. Tolerance on MAB Position.  The plot shows the average uncertainty in reconstructed chamber locations as a function of the uncertainty estimate on the determination of the placement of the MABs within CMS.

The correlation between ME (1 chambers and the Secondary Link lines is likely to be strong for ME (1/2 chambers, but weaker for ME (1/3 chambers, as the ME (1/3 chambers reconstruction relies strongly on MABs.  Figure 3.6 shows the uncertainty of reconstructed RPhi chamber location in ME (1 as a function of Secondary Link line definition.  As expected ME (1/3 chambers show very little change as the Secondary Link line resolution is varied.  Surprisingly, the coupling of the Secondary Link line resolution and the ME (1/2 chambers is non-linear.  This is most likely due to either the dominance of other errors in the reconstruction of ME (1/2 chambers when the Secondary Link line is well defined, or an indication that ME (1 SLM reconstruction is more complicated than previously thought.

Figure 3.6:  Reconstructed CSC RPhi Chamber Uncertainty vs. Secondary Link Line Resolution.  The plot shows the average uncertainty in reconstructed chamber locations as a function of the uncertainty estimate on the placement of the Secondary Link Line.

#### DCOPS-Reference Center Tolerance

Figure 3.7 shows how the uncertainty in the CMS RPhi position of the CSC chambers vary with the uncertainty in the chamber construction (along the chamber’s local X axis).  For all chambers, this relationship is linear. The slope indicates the correlation between uncertainties in chamber construction and reconstructed chamber RPhi positions is roughly 1:3, except on the ME (1/2 chambers where it is closer to 1:4. The significantly higher correlation on the ME (1/2 chambers is due the much lower uncertainties associated with the definition of the Secondary Link lines and resolution of the ME (1/2 LINK CMOS sensors.  Correlations decrease slightly for chambers located in ME layers further away from the MABs as the net uncertainty is generally larger (See Figure 3.5).

Figure 3.7:  Reconstructed CSC RPhi Chamber Uncertainty vs. DCOPS-CSC Reference Center Tolerance.  The plot shows the average uncertainty in reconstructed chamber locations as a function of the uncertainty estimate on the relative placement of the primary DCOPS calibration pin with the chamber reference centerpoint.

#### DCOPS Pixel Resolution

DCOPS sensors make measurements by fitting the charge distribution across the CCD pixel arrays.  Each pixel in the array is approximately 14 µm wide.  The resolution of the DCOPS sensors is in large part determined by the quality of the fit and the shape of the distribution to be fit.  Typical short term fluctuations in the fitted centroids during the 2001 ISR tests suggested that the short term resolution of the DCOPS sensors in the ISR tunnel to be on the order of 1 pixel, however it is certainly possible that the conditions in the CMS detector will decrease the stability of these measurements.  Figure 3.8 shows the uncertainty in the reconstructed chamber RPhi locations as a function of DCOPS pixel resolution.  As the figure indicates, an uncertainty of up to three pixels in the location of the centroids still provides a resolution of better than 250 (m on the reconstruction (in CMS RPhi) of chamber centers.  The independence of ME ±1/2 chambers in Figure 3.8  is expected since the measurement devices are not DCOPS sensors (thus no CCD pixel resolutions to degrade).  The uncertainties in ME ±1/2 chamber locations are plotted to illustrate the independence of these chambers to degraded measurements in ME ±1/3 chambers positions.

Figure 3.8:  Reconstructed CSC RPhi Chamber Uncertainty vs. DCOPS Pixel Resolution.  The plot shows the average uncertainty in reconstructed chamber locations as a function of DCOPS pixel resolution.  One pixel is 14 µm wide.  ME (1/2 chamber sensors are not DCOPS sensors and have not been varied.

#### ME (1/2 Inclinometer Resolution

Although it was quickly established that the inclusion of inclinometers were required on ME (1/2 chamber frames, it was unclear if the use of the same inclinometers on the transfer plates would provide sufficient resolution (as well as a sufficient margin of safety) to successfully reconstruct chamber locations.  A series of simulations was performed to investigate the dependence of ME(1 chamber reconstruction on inclinometer resolution.  Figure 3.9 shows the dependence of the uncertainty in the determination of reconstructed CMS RPhi ME (1chamber positions as a function of ME (1/2 inclinometer resolution. The uncertainty in the ME (1/2 chamber RPhi location is seen to approximately double in a linear as the fashion inclinometer resolution is varied from its nominal short term resolution to the long term resolution. ME (1/3 RPhi chamber resolution remains roughly independent of the inclinometer resolution, though, as Table 3.7-Table 3.10 indicate, there are other chamber parameters which depend upon the resolution of the inclinometers.

Figure 3.9  ME±1 CSC Chamber Resolution vs ME±1/2 Inclinometer Resolution.

The determination of the ISR inclinometer resolutions used in the simulation is based upon the results of the extended, uncorrelated, and uncorrected measurements over the approximately three months of testing during the 2000 ISR Tests.  It is likely that further work with these inclinometers will increase the precision of these measurements.

## Conclusions

The results garnered from COCOA simulations of the Idealized EMU System indicate that the design of the EMU Alignment scheme is viable and can reconstruct chamber locations along SLM lines with an uncertainty of ≈200μm in CMS RФ and ≈500μm in CMS Z.  A detailed error analysis and subsequent examination of key sources of uncertainties across several simulations show that the tolerances on component construction and DCOPS calibration are well understood and meet the necessary requirements to ensure the successful reconstruction of chamber positions.

Although the simulation assumes the entire system operates perfectly (unlikely for any complex system), in many cases the estimations of uncertainties and tolerances in components  modeled in the simulation have been very conservative (symmetrizing asymmetric tolerances, assuming little or no additional calibration on CSC chambers, taking long term uncorrelated resolutions of ISR sensors).  It is also likely that several sets of measurements could be simultaneously fit in the COCOA simulation to compensate for failed or damaged components.  More importantly, the additional knowledge about components in the system acquired over the next 3-5 years prior to the commissioning of the CMS detector is likely to further constrain the fits made by COCOA and further minimize the uncertainties associated with the reconstruction of SLM sensors and CSC chambers.