POLAR Spacecraft Status As of: Tues, 6 Dec 05, 15:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:56=AN STIP data only | NOAA-14J AM: 20:57=AN STIP data only | NOAA-15K AM: 17:57=AN GAC data only | NOAA-16L PM: 14:54=AN GAC&LAC data | NOAA-17M AM: 22:24=AN GAC&LAC data | NOAA-18N PM 13:54=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU-1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ Investigating instability | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate ROLL Rgmode=PASSIVE Gyro-1 Off 10/24/05 Gyro-3 Off 6/10/04 Gyro chans XA-ZB TOAR 454 RGyro roll estimate gains updated 11/17 | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation Probable collision on 20 Nov at 10:31z | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Momentum shift transition started 1 Nov ended 18 Nov. |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/3/03) #2 has 3 chans inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 OFF OFF 13Nov-13Dec | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 omni=rcp Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/05 Full Sun Sun Angle 16 up to 22 in early Jan Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -50 Batts 1&3V/T=6/9 Batt2 VT=7/9 Since 11/22/05 Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Degraded shunts SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 14 Up to 15 mid-Dec Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 41 Start new uptrend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Erratic Frequent scan motor current surge Occasional imagery bar codes Channels 2&4 APT | Nominal Rare major scan motor surges. Last Incident 11/18/04 Reduced stability last week | Variable Nominal last week No bar codes since 12 Oct. TCE24 OFF 4/14/04 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal 7/12/05 FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 CLOSED Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment. | Operational Status downgraded to Yellow 15 Aug 05 LW channel 1-12 noise TOAR 448 LW Noise improved since 14 Oct Problem isolated to loose LWIR lens |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 Investigating change in motor current trend |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU8 off TOAR 449 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 as of 27 Sept | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous TED shutdown 24 Sept | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	There were no changes to N12 during the past reporting period.

NOAA-14:	The N14 AVHRR scan motor continues to experience frequent (several per day) current spikes that affect imagery

primarily by causing occasional bar codes on HRPT images.   Synch delta is also highly variable but does seem to benefit rephase enable operation that is executed out of stored commands over the South Pole each orbit (illustration 1).

Power balance appears to have maintained optimization during the past week with generally stable bus voltages, and much lower average shunt driver voltages (illustration 2).  Otherwise there was no change to N14 during the past week.

NOAA-15:	N15 VTX-1 (APT data) remains off until 13 Dec because of an RF conflict with N12.  One item of note on N15 was the AVHRR scan motor current which surged approximately 8 mAmps on 28 Nov but, unlike recent previous experience, has not yet quite stabilized.  At the moment, the N15 AVHRR scan motor (which has experienced several severe anomalies in the past 5 years) is operating at its highest scan motor current value since August of 2004. On the positive side, imagery, synch delta and AVHRR component temperatures all remain stable and nominal (illustration 3 and 4).  Otherwise, the other payloads on N15 were nominal during the past week (illustration 5 for HIRS health depictions and  illustration 6, for AMSU’s) as was the rest of the spacecraft (illustration 7 depicts ADACS health.)

NOAA-16:	The N16 AVHRR scan motor current, unlike N15’s, AVHRR fell to its lowest (most nominal) value in many months

this week and is now within what has historically been considered a perfectly nominal value range (illustration 8).  This assessment is further reinforced by the fact that wave patterns in the HRPT images have recently begun to disappear (bar codes and MIRP frame losses have been absent for several months already) and synch delta is also in a nominal range (illustration 9 & 10).  We’ve been here before however, and the only constant that can be expected from this payload is its performance variability.  Otherwise, all other N16 payloads were nominal last week although the HIRS continues to operate with a filter motor current at or near all time high values with no reports of imagery degradation. (Illustration 11 depicts the AMSU’s and illustration 12 the HIRS.)

The N16 ADACS subsystem remained stable within improved values after the uploaded of updated Rgyro roll estimation filter gains on 17 Nov into the control CPU (only).  Without doubt, the new gains improved and stabilized the Y-wheel situation significantly (illustration 13 and 14).  However, the temps and currents on this wheel remain historically very elevated (illustration 15) and are expected to remain so for the duration of the mission.  On the other hand, with the improvement of N16 roll rates and errors and Y-wheel motor currents and temperatures sustained over the past 18 days it is now assumed that this update is a success and will be made permanent by commanding it into the non-control CPU sometime this week.  Originally, the new gains were only installed on the control CPU in case of instability.  If the new gains had threatened attitude performance, a switch of control to the backup CPU (which still had the old gain values) would have maintained spacecraft attitude.  See illustration XY for depictions of the sustained stability of N16 roll axis performance.

NOAA-17:	There was basically no change to N17 during the past week.  The remaining two AMSU’s (illustration 16) and the

HIRS operated within the same general nominal values that they did the previous week while the AVHRR scan motor current continued to show some minor instabilities which remain (and hopefully will continue to remain) well within nominal values (illustration 17).  The spacecraft attitude situation remained unchanged from last week manifesting absolutely no residual effects from the collision it experienced on 20 Nov (see write-up in last weeks report) with a small particle of space debris (illustrations 18 and 19 ).   No further operational actions or reconfigurations are expected to take place in regard to that event.

NOAA-18:	The N18 payload suite was nominal and stable during the past week (illustrations 20 and 21).  The MHS

flywheel motor which had recently demonstrated a new trend increase in motor current appeared to have possible “topped out” during the past week (illustration 22).  This situation, reported in last weeks report, was brought to the attention of EUMETSAT engineers because of concerns that the bearings were possibly wearing out.  EUMETSAT engineers analyzed the data and concluded that this component remains nominal and that the trend change is a feature of this component which has been seen previously on a test MHS unit during a 5 year extended life test which was performed between 1997 and 2002.  In response to this trend change, EMOSS will increase its vigilance over this component as a matter of caution.

The N18 attitude situation is again in equilibrium now that the Z-(pitch) momentum shift (and wheel rotation counter shift) process is complete with all components operating nominally  (illustration 23).

EMOSS personnel supported a meeting called by ITT at which the N18 HIRS long wave channel (NEdN) degradation problem was addressed (TOAR 448).  This problem with this payload is an out of family behavior that causes it to be hypersensitive to dynamic disturbances (such as solar array slews).  According to the briefing package, the slow radiometric drift following a recent solar array slew pointed out that the radiance from the scene was changing.  This required an optical throughput change which means an optical element in the LWIR must be moving.  Optical modeling and testing assessed many possible root causes that fit the on orbit radiometric characteristics but the only fault that fit all the conditions was a loose L1 relay lens.  No on-orbit reconfigurations can be implemented to correct for this situation and any future solar array offset reconfigurations are likely to negatively affect products from this component for a significant duration of time.

Illustration 1:  NOAA-14 AVHRR Health Analysis

(No different than the last several weeks.)

Illustration 2:  NOAA-14 EPS Health Analysis

(Remaining stable and nominal since the recent solar array offset alteration.)

Illustration 3:  N15 AVHRR Health Analysis

(Scan motor current starting to look somewhat negative, upper right plot, and is operating at its highest level since Aug 2004, lower left plot.  On the positive side, temperatures and synch delta values remains stable.)

Illustration 3:  N14 EPS Analysis (part 2)

(No problems in the battery thermal situation as a result of the VT change either.)

Illustration 4:  N15 AVHRR Imagery Analysis

(Also on the positive side, imagery remains nominal.)

Illustration 5:  N15 HIRS Health Analysis

(Continues to operate within the most stable and nominal values in the last half decade.)

Illustration 6:  N15 AMSU Health Analysis

(Nominal and stable.)

Illustration 7:  N15 Attitude Control Analysis

(Generally nominal and stable.)

Illustration 8:  N16 AVHRR Health Analysis

(Back to nominal last week, but for how long?)

ILLUSTRATION 9:  N16 Synch Delta Analysis

(Nominal and stable, no MIRP rephases required since mid-November.)

RE=MIRP

Rephase Enable

Operation.

ILLUSTRATION 10:  N16 AVHRR Imagery Analysis

(Wave patterns starting to disappear from HRPT images for the first time in many months.  No bar coded imagery since mid-October.)

ILLUSTRATION 11:  N16 AMSU Health Analysis

(Nominal and stable.)

Illustration 12:  N16 HIRS Analysis

(Remaining at or near all time high filter motor current values as well as high low amplitude ranges.  Remains on the “watch list”.)

Illustration 13:  N16 ADACS Health Analysis (Part 1)

(Remaining very stable since the new gain updates went into effect several weeks ago following the failure of a second gyro.)

Illustration 14:  N16 ADACS Health Analysis (Part 2)

(Again very stable since the new gain updates went into effect.)

Illustration 15:  N16 RWheel Effect of New Rgyro Pitch Estimation Gains

(An obvious improvement, enough to make the change permanent, following the failure of gyro-1 but still a long way from what had been previously.)

Illustration 16:  N17 AMSU Health Analysis

(Nominal and stable, just like last week.)

Illustration 17:  N17 AVHRR Health Analysis

(Generally nominal and stable notwithstanding a little instability from the scan motor current in the past several weeks, including this week.)

Illustration 18:  N17 ADACS Analysis

(Nominal and stable all week no long term effect from the collision.)

Illustration 19:  N17 ADACS Health Analysis (Part 2)

(As stated in previous illustration, no long term impact apparent.)

Illustration 20:  N18 AMSU Health Analysis

(Nominal and stable.)

Illustration 21:  N18 AVHRR Health Analysis

(Nominal and stable.)

Illustration 22:  N18 MHS Analysis

(Flywheel current increase seems to have topped out but remains less stable than it has historically been.)

Illustration 23:  N18 ADACS Analysis

(Generally nominal and stable, notwithstanding the TOAR on the Z-pitch wheel.)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING December 2, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 11/25 | -908 msec | +279 msec | -350 msec | +353 msec | +179 msec | +131 msec |
| SAT. 11/26 | N/A | +280 msec | -352 msec | +355 msec | +180 msec | +131 msec |
| SUN. 11/27 | N/A | +281 msec | -349 msec | +355 msec | +182 msec | +131 msec |
| MON. 11/28 | -914 msec | +282 msec | -352 msec | +354 msec | +182 msec | +134 msec |
| TUE. 11/29 | -914 msec | +282 msec | -352 msec | +355 msec | +183 msec | +134 msec |
| WED. 11/30 | -414 msec * | +278 msec | -352 msec | +357 msec | +183 msec | +136 msec |
| THU. 12/01 | -414 msec | +280 msec | -355 msec | +356 msec | +184 msec | +137 msec |

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of -500 milliseconds on 09/15/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 11/30/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will occur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next -500 millisecond jump is expected on 02/14/06.