1)  More Voltage-Tap Channels (priority 1)

1A)  More Cryostat Access Wires:

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | No hassle, no risk. | Lose info on quench-origin. |
| Add wires: | No risk to present system. | More heat load, difficult. |
| Replace “1.8K-direct wires” with more, smaller Cu wires: | Quick, cheap. | More heat-load to 1.8K. |
| Replace “1.8K-direct wires” with more, bronze wires: | Less heat load to 1.8K reservoir. |

Some bronze-wire risk.

No room for strain-gage wires.

Replace all V-tap wires with bronze.

Min. heat to both systems.

| Room for strain-gage wires. | Maximum bronze-wire risk. |
| --- | --- |

Plan: Option #5, to minimize the anomalously large heat-load by the maximum amount.

1B)  More Amplifier Access Wires:

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | No hassle, no risk. | Lose info on quench-origin. |
| Add RG-58 wires: | No risk to present system. |

Bulky, not twisted-pairs.

Requires SHV panel at cryostat

| Replace RG-58 tangle with shielded twisted wires: | Improve signal/noise ratio. | More work. |
| --- | --- | --- |

Plan: Option #3, to improve the chances of getting a meaningful measure of the splice resistance.

1C) More Quench-Origin Amplifiers:

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | No hassle, no risk. | Lose info on quench-origin. |
| Add derivative amplifiers: |

Easy derivative data.

| High frequency data for free. | New derivative amplifiers: made/finished/calibrated. |
| --- | --- |
| Add old conventional amplifiers: | Some old amplifiers available. | More difficult derivative info. |
| Add SSC conventional amplifiers | Won’t have to build or fix as many amplifiers. |

May not come in time.

Some extra work to utilize.

Plan: A combination of options 2, 3, 4, to minimize the effort required to get a full set of data.

1D) Splice Amplifiers:

| Option | Plus | Minus |
| --- | --- | --- |
| Use conventional amplifiers: | Min. hassle, min. cost. | Probably no splice info . |
| Install high-gain amplifiers immediately above cryostat: | Improved chances of getting readable signal. | Additional equipment and maintenance costs. |
| Install high-gain amplifiers inside cryostat: | Best signal/noise ratio. | Additional equipment and maintenance costs. |

Plan: Option #2, with a high amplifier gain (G > 1000) and easy (remote) offset adjustment.

1E) More Data-Logger Channels:

| Option | Plus | Minus |
| --- | --- | --- |
| Live with 64 channels: | Min. hassle, min. cost. | Lose info on quench-origin. |
| Install a third block: | Full 96 channel capability. | Need DAQ/Viewer channel capacity upgrade. |
| Install a third block plus back-up capability: | Best chance of maintaining full capability during test. | Above , plus additional storage and transfer costs. |

Plan: Option #3, for maximum insurance against hardware failure; but settle for option #2.

1F) Data-Acquisition Upgrade:

| Option | Plus | Minus |
| --- | --- | --- |
| Collect only channels 1-64: | Min. hassle, min. cost. | Lose info on quench-origin. |
| Acquire a third data-block with GETDATA: | Full 96 channel capability. |

More data-storage space used.

Minor software modifications.

Acquire all V-tap data via LabView:

Windows capability.

| Test future capability now. | Major software modifications. |
| --- | --- |

Plan: Option #2, to minimize the effort to store all the data.

1G) Data-Viewer Upgrade:

| Option | Plus | Minus |
| --- | --- | --- |
| View only channels 1-64: | Min. hassle, min. cost. | Lose info on quench-origin. |
| Read 64 channels at a time: | Minimum software change. | Probably inconvenient. |
| Read 96 channels at a time: | Convenient data access. | No QBX capability likely. |
| Read all V-tap data via LabView: |

Windows capability.

| Test future capability now. | Major software modifications. |
| --- | --- |

Plan: Option #3, to minimize the effort to read all the data; settle for option #2.

2)  More Strain-Gage Channels (priority 1)

2A) More Cryostat Access Wires:

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | Min. hassle, min. cost. | Lose info on coil strains, or lose cryostat diagnostics. |
| Add wires: | No risk to present system. | More heat load, difficult. |
| Replace “1.8K-direct wires” with more, smaller Cu wires: | Quick, cheap. | More heat-load to 1.8K. |
| Replace “1.8K-direct wires” with more, bronze wires: | Less heat load to 1.8K reservoir. | Some bronze-wire risk. |
| Run all S-gage wires along-side new bronze V-tap wires. |

Min. heat to both systems.

| Neatest 300K transition. | Maximum bronze-wire risk. |
| --- | --- |

Plan: Option #5, to minimize the total heat-load to 1.8K and 4.5K systems.

2B) More Scanner Access Wires: (Ready for testing)

2C) More Scanner DAQ-Channels: (Ready for testing)

2D) More Scanner Read-Channels: (Ready for testing)

3)  More Temperature Channels (priority 2)

3A) More Cryostat Access Wires: (same as strain-gage)

3B) More Scanner Access Wires: (same as strain-gage)

3C) More Scanner DAQ-Channels:

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | Min. hassle, min. cost. | Borrow channels. |
| Add another scanner: | Get full signal complement. |

More data,

Slower DAQ.

DAQ software upgrade.

Plan: Option #2, for maximum data.

4) Magnet Transport/Restraint System (priority 1)

4A) 2000 Pound Pusher/Puller:

| Option | Plus | Minus |
| --- | --- | --- |
| Ball screw: |

Easy power-assist.

Easy direction reversal.

No forces on sealing surfaces.

Bulky (1.5x magnet length).

Interference with diagnostics.

Pushing???

| Reach??? |
| --- |
| Block & Tackle: | Useable for B58 transport. |

Cumbersome.

Danger to diagnostics.

Come-Along:

Small space requirement.

Useable for B58 transport.

Cumbersome.

Protection for sealing surface.

Electric winch:

Convenient operation.

| Useable for B58 transport. | More expensive. |
| --- | --- |

Plan: Option #4, for maximum ease and flexibility. Winch is capable of being bolted to the floor or the cryostat.

4B) 90-Degree Transport Capability:

| Option | Plus | Minus |
| --- | --- | --- |
| Present cart & pry-bars: | Min. hassle, min. cost. | No 90 degree capability. |
| Leap-frogging ball plates, with winch: |

Multi-directional.

Minimal friction.

Leap-frogging ball-plates.

Rolls too easily.

Hard to control direction.

Leap-frogging ground-plates.

Steerable, corner-mounted roller-wheels, with winch:

Steerable.

Safer.

Easy height/angle adjustment.

Steering coord. required??

Steering causes translation??

Leap-frogging ground-plates.

Plan: Option #3, with electric or drill-operated winch.

4C) Angle/Height Mating Adjustment System:

| Option | Plus | Minus |
| --- | --- | --- |
| Shims & pry-bars: | Min. change, min. cost. |

Time consuming.

| Dangerous?? |
| --- |
| Two (front) jacking screws: | Easy height adjustment. | Imprecise transverse adjust. |
| Corner jacking screws on independent roller-plates: |

Relatively easy transverse movement.

| Easy height adjustment. | “Stumbling” problem?? |
| --- | --- |
| Corner jacking screws on railed roller-plates: | Less “stumbling problem. | More parts. |

Plan: Option #3, for maximum adjustment capability, with #4 as a back-up.

4D) Insertion/Removal Friction Reduction Alterations:

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | Min. hassle, min. cost. |

Excessive friction.

| Potential insertion delay. |
| --- |
| Third rail: | Potentially less friction. |

Requires rework of cryo-diagnostics/protection system.

| New parts needed. |
| --- |
| Reassemble present rails with thrust washers: | Potentially less friction. |

Considerable labor.

Danger to diagnostics.

Protection for sealing surface.

Replace cylinder rollers with balls in a groove:

Potentially less friction.

| Self aligning. | New parts needed. |
| --- | --- |

Plan: Evaluate present system with 2000# LBQF1. Extrapolate to D20 and modify as needed to stay below 1500# pull.  Evaluate extrapolation assumptions with D19B (5000#).

4E) Seismic Restraint:

| Option | Plus | Minus |
| --- | --- | --- |
| Current (frozen grease): | Min. hassle, min. cost. | Danger to end-domes. |
| Pinned, hard end-stops: | Relatively easy. | Rail damage with big quake. |
| Pinned, end-stop springs: | Less rail damage?? | Locate springs |

Plan: Option #3, for maximum safety; but settle for #2.

5) Miscellaneous Improvements:

5A) North-End Extension Umbilical (priority 3)

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | Min. Hassle; Min. effort. | More labor and risk every magnet change. |
| North-end access only: | Less magnet change labor/risk. | Lacks flexibility. |
| Mirror image: |

Less magnet change labor/risk.

Maximum flexibility

More effort

Less north end radial clearance.

Plan: Option #3, for maximum ease and flexibility.

5B) LHe Displacer (priority 3)

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | Min. Hassle; Min. Effort. |

Expensive if no user ready.

| Slow sub-cooling. |
| --- |
| Logs of Stycast coated ping-pong balls: | Recovers capital investment. |

Might fail.

Not optimum displacer.

Logs of teflon-sealed tubing:

Better displacer.

| Auto-pressure relief. | More cost. |
| --- | --- |
| Logs of teflon-sealed hexagonal tubing: |

Best displacer.

| Auto-pressure relief. | More cost. |
| --- | --- |

Plan: Option #3, for maximum ease and flexibility.

6) Cryo-System Maintenance

6A) Priority 1:

Install two check-valves down-stream from Auto Kick-Back regulator.

Fix leak detector.

Check/replace belts on sub-cooling pump.

Prepare 80K bed.

Fix east ion-gage.

Check WX leak-rates.

Check DX leak-rates.

6B) Priority 2:

Change compressor room R-V from 5psi to 10 psi.

Add vacuum relief valve around roughing pump.

Graph data from subcooling system flow-test.

Graph data from cryo system pressurized leak-test.

Assemble spare DX.

Update procedural manual.

Install DX hydraulic pressure transducers.

6C) Priority 3:

Install differential-pressure gauge across Make-Up filter.

Improve LN control system.

Calibrate each ion gage with its controller.

Make protective box for Mag. Meas. bench.

Change Make-Up regulator gauges to 100psi (max.).

Repair leak in DX hydraulic system; add oil.

Record distance of dead-bands in LHe level gauges.

Replace R-V’s and gauges on roof-tanks.

7) DAQ-System Maintenance

7A) Priority 1:

7B) Priority 2:

7C) Priority 3:

8) Operating-System Maintenance

8A) Priority 1:

8B) Priority 2:

8C) Priority 3: