# UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

# WASHINGTON, DC 20460

OFFICE OF  PREVENTION, PESTICIDES,  AND TOXIC SUBSTANCES

DRAFT

Triclosan

Occupational and Residential Exposure Assessment

Office of Pesticide Programs

Antimicrobials Division

U.S. Environmental Protection Agency

Date: April 17, 2008

TABLE OF CONTENTS

EXECUTIVE SUMMARY	3

1.0	 INTRODUCTION	6

1.1	Purpose	6

1.2	Criteria for Conducting Exposure Assessments	6

1.3	Chemical Identification	8

1.4	Physical/Chemical Properties	8

2.0	 USE INFORMATION	8

2.1	 Formulation Types and Percent Active Ingredient	8

2.2	 Summary of Use Pattern and Formulations	9

3.0	SUMMARY OF TOXICITY DATA	9

3.1	Acute Toxicity	9

3.2	Summary of Toxicity Endpoints	10

3.3	FQPA Considerations	12

4.0	RESIDENTIAL EXPOSURE ASSESSMENT	12

4.1	Summary of Registered Uses	12

4.2	Residential Exposure	12

4.2.1	Residential Handler Exposures	13

4.2.2	Residential Post-application Exposures	15

4.2.2.1	Textiles………………………………….……………………..…………………………...… 15

4.2.2.2	Plastic (Toys)………...……….………….…………………………………………………... 19

4.2.3	Data Limitations/Uncertainties……………………………………………………………….20

5.0	RESIDENTIAL AGGREGATE RISK ASSESSMENT AND CHARACTERIZATION 	21

6.0	OCCUPATIONAL EXPOSURE ASSESSMENT	21

6.1 	Occupational Handler Exposures	22

6.2  	Occupational Post-application Exposures	25

6.3	Data Limitations/Uncertainties	25

7.0	REFERENCES	25

EXECUTIVE SUMMARY

This document is the Occupational and Residential Exposure Chapter of the Reregistration Eligibility Decision (RED) document for triclosan. It addresses the potential risks to humans that result from the use in occupational and residential settings.  Although individual EPA-regulated uses have been assessed using standard Agency methodology within this chapter, the National Health and Nutrition Surveys (NHANES) biological monitoring data are available for assessing aggregate exposure and risk. Therefore, although this human exposure chapter for the triclosan RED characterizes exposures from individual EPA-regulated uses, EPA views the NHANES data as more representative of aggregate exposures to determine probability of co-occurrence of EPA and FDA-regulated uses.

Triclosan is used as a bacteriostat, fungistat, mildewstat, and deodorizer. The EPA registered products containing triclosan as the active ingredient (ai) are formulated as ready-to-use, pelleted/tableted, emulsifiable concentrate, soluble concentrate, and impregnated materials. Concentrations of triclosan in these products range widely from 0.69% to 99%.  The EPA registered products are used in commercial/ institutional/industrial, residential and public access, and material preservatives.  The residential use includes a direct application to HVAC coils (limited to commercial applicators).  Additionally, triclosan is registered to be used as a material preservative in such products as paints (in-can preservative), polymers and plastics (e.g., toys, tooth brushes, etc), and textiles (e.g., footwear, clothing, etc).  There are many other FDA uses (e.g., hand soaps, toothpaste) that are not under EPA’s regulatory jurisdiction but for which reliable exposure data are available (U.S. Food and Drug Administration, OTC docket 81N-033P, Vol. 41).   These exposures have been considered in the aggregate risk assessment within the risk assessment chapter for triclosan.  However, the FDA uses are not assessed in this chapter.

The durations and routes of exposure evaluated in this assessment include short-term (ST) and intermediate-term (IT).  The inhalation endpoint (ST/IT durations) is based on a 21-day rat inhalation study with a LOAEL of 50 mg/m3 equivalent to 3.21 mg/kg/day.  The adverse effect for this endpoint is based on increased total leukocyte count and increased serum alkaline phosphates observed in the male.  For the incidental ingestion exposure scenarios, the ST/IT oral endpoints (30 mg/kg/day) are based on adverse effects of clinical signs of toxicity include vomiting, failure to eat, and diarrhea in a chronic toxicity study in Baboons.  No short-term dermal endpoint for systemic effects was selected for triclosan, since no systemic effects were identified. A short-term dermal irritation endpoint was identified. The short-term irritation endpoint was determined from a 14-day dermal toxicity in mice.  Irritation was observed at 0.6 mg/kg/day equivalent to 100 μg/cm2.  The dermal study was based on a 99% ai formulation.  The residential uses of triclosan are the result of diluted formulations.  Therefore, the short-term dermal irritation observed for the 99% ai formulation was not appropriate for the dermal risk assessment.  The intermediate-term dermal endpoint was determined from the 90-day dermal rat study.  The route-specific dermal NOAEL from this study is 40 mg/kg/day.  Because the toxicological endpoints selected for inhalation, dermal, and oral routes of exposure are not female-specific, a body weight of 70 kilograms is used in the assessment.  EPA’s level of concern (LOC) for occupational and residential triclosan dermal and oral routes of exposures is 100 (i.e., a margin of exposure (MOE) less than 100 exceeds the level of concern). The level of concern is based on 10x for interspecies extrapolation and 10x for intraspecies variation.  The LOC for the inhalation route of exposure is 1000 based on10x for interspecies extrapolation, 10x for intraspecies variation, and a 10x for the use of a LOAEL.

This occupational and residential assessment was based on examination of product labels describing their uses.  It has been determined that exposure to residential handlers is restricted to the registered end use product that is for paint containing triclosan as an in-can preservative.  Occupational handlers may be exposed in the manufacturing of other products (e.g., plastics, textiles) and during commercial HVAC coil applications and commercial painters.  Additionally, post-application exposures are likely to occur in residential settings from contacting treated articles such as clothing and plastic toys.  The representative scenarios selected by EPA for assessment were evaluated using maximum application rates as stated on the product labels.  The representative scenarios are believed to represent high-end uses resulting in dermal, inhalation, and incidental oral exposures.

To assess the handler risks, EPA used surrogate unit exposure data from the Chemical Manufacturers Association (CMA) antimicrobial exposure study and the Pesticide Handlers Exposure Database (PHED).  Post application/bystander exposures were assessed using EPA’s standard assumptions (e.g., Health Effects Division’s (HED) Standard Operating Procedures (SOPs) for Residential Exposure Assessment).

Residential Handler Risk Summary

Dermal

The residential handler dermal exposure scenarios are best represented by the short-term duration (i.e., painting is intermittent in nature).  The short-term dermal duration toxicological endpoint is based on dermal irritation observed during the dosing of mice with a 99% ai product.  The in-can paint preservation (1 % ai) is not considered to be as irritating as the more concentrated test substance.  Therefore, the residential handler assessment does not include the dermal pathway.  The short-term dermal exposures are believed to exhibit minimal skin irritation risk.

Inhalation

For the residential handler inhalation assessment, the inhalation risks were calculated by comparing the daily inhalation dose to the short-term inhalation endpoint.  The inhalation MOEs were above the target MOE of 1000 for the paint brush scenario but below the target MOE for the airless sprayer, and therefore, is of concern.

Residential Post Application/Bystander Risk Summary

Dermal & Oral

The residential post-application intermediate-term dermal and short- and intermediate-term incidental oral risks were assessed for children and/or adults coming in contact with treated clothing and plastic toys.  The treated clothing was used to represent exposure to triclosan-treated mattresses.  No risks were identified for these uses.  The MOEs were equal to or greater then the target MOEs.

Inhalation

Based on the low vapor pressure of triclosan and the lack of aerosol generation over time by the application methods, inhalation exposure is expected to be minimal.

Occupational Handler Risk Summary

Dermal

The short-term dermal irritation exposures and risks were not estimated for occupational handler exposures.  Instead, dermal irritation exposures and risks will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.

For the intermediate-term dermal risks, the MOE were above the target MOE of 100, and therefore, not of concern except for commercial painters and material preservative use for paper.  The intermediate-term MOEs for using a paint brush/roller and an airless sprayer are 31 and 1, respectively.  Because triclosan is used as a material preservative in the paint, the use of chemical resistant gloves on the label is impractical.

Inhalation

For the occupational handler inhalation exposure and risk assessment, the MOEs were below the target MOE of 1000 for all scenarios except for the brush application for paints.  The inhalation MOE for commercial use of an airless sprayer for paints is 54, for liquid pour and liquid pump during paint manufacturing 330 and 290, respectively, and for pulp and paper the metering pump is 28.

Occupational Post Application/Bystander Risk Summary

Based on the low vapor pressure of triclosan and the lack of aerosol generation over time by the application methods, inhalation post-application exposure are expected to be minimal.

Data Limitations and Uncertainties:

There are a number of uncertainties associated with this assessment and these have been reiterated from Sections 4.2.3 (residential) and 6.4 (occupational).  The major data limitations and uncertainties associated with the exposure assessments include the following:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix A for summaries of these data sources). Most of the CMA data are of poor quality therefore, EPA requests that confirmatory monitoring data be generated to support the values used in these assessments.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA 2000, and 2001).  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on EPA estimates and could be further refined from input from registrants.

1.0	 INTRODUCTION

## 1.1	Purpose

In this document, EPA’s Antimicrobials Division (AD) presents the results of its review of the potential human health effects of occupational and residential exposure to triclosan (5-chloro-2-(2,4 dichlorophenoxy) phenol). This information is for use in EPA's development of the triclosan Reregistration Eligibility Decision (RED) document.

## 1.2	Criteria for Conducting Exposure Assessments

An occupational and/or residential exposure assessment is required for an active ingredient if (1) certain toxicological criteria are triggered and (2) there is potential exposure to handlers (mixers, loaders, applicators, etc.) during use or to persons entering treated sites after application is complete.  For triclosan, both criteria are met. Toxicological endpoints were selected for short- and intermediate-term dermal, inhalation, and incidental oral exposures to triclosan.  There is the potential for exposure in a variety of occupational and residential settings.  Therefore, risk assessments are required for occupational and residential handlers as well as for occupational and residential post application exposures that can occur as a result of triclosan use.

In this document, handler scenarios were assessed by using unit exposure data to estimate occupational and residential handlers’ exposures. Unit exposures are estimates of the amount of exposure to an active ingredient a handler receives while performing various handler tasks and are expressed in terms of micrograms or milligrams (1 mg = 1,000 µg) of active ingredient per pounds of active ingredient handled.  A series of unit exposures have been developed that are unique for each scenario typically considered in assessments (i.e., there are different unit exposures for different types of application equipment, job functions, and levels of protection).  The unit exposure concept has been established in the scientific literature and also through various exposure monitoring guidelines published by the USEPA and international organizations such as Health Canada and OECD (Organization for Economic Cooperation and Development).

Using surrogate unit exposure data, maximum application rates from labels, and EPA estimates of daily amount handled, exposures and risks to handlers were assessed.  The exposure/risks were calculated using the following equations:

Daily Exposure: Inhalation and dermal handler exposures are estimated for each applicable handler task with the application rate, quantity treated/handled in a day, and the applicable inhalation unit exposure using the following formula:

Daily Inhalation or dermal Exposure:	E = UE x AR x AT			(Eq. 1)

Where:

E	=	Amount (mg ai/day) that is available for inhalation and dermal exposure;

UE	=	Unit exposure value (mg ai/lb ai) derived from August 1998 PHED data or from 1992 CMA data;

AR	=	Maximum application rate based on a logical unit treatment, such as acres (A), square feet (sq. ft.), gallons (gal), or cubic feet (cu. ft). Maximum values are generally used (lb ai/sq ft, lb ai/gal, lb ai/cu ft); and

AT 	=	Normalized application area based on a logical unit treatment such as square feet  (sq ft/day), gallons (gal/day), or pounds of articles/products to be treated for material preservatives.

Daily Dose: The inhalation dose is calculated by normalizing the daily exposure by body weight and adjusting, if necessary (not needed for triclosan because of the availability of a dermal route-specific study), with an appropriate dermal absorption factor.  An absorption factor of 100% was used for inhalation exposures because there are no data available to refine this variable.  Daily dose was calculated using the following formula:

Daily Dose:	ADD = E x ABS							(Eq. 2)

BW

Where:

ADD 		= 	Average daily dose or the absorbed dose received from exposure to a chemical in a given scenario (mg active ingredient/kg body weight/day);

E 		=	Amount (mg ai/day) that is available for inhalation or dermal exposure;

ABS 		= 	A measure of the amount of chemical that crosses a biological boundary such as lungs (% of the total available absorbed); and

BW		= 	Body weight determined to represent the population of interest in a risk assessment (kg).

Margins of Exposure:  Non-cancer inhalation risks for each applicable handler scenario are calculated using a Margin of Exposure (MOE).  This is the ratio of the daily inhalation dose or dermal dose to the toxicological endpoint of concern.

Margins of Exposure:			MOE = NOAEL or LOAEL			(Eq. 3)

ADD

Where:

MOE 			= 	Margin of exposure, value used to represent risk or how close a chemical exposure is to being a concern (unitless);

NOAEL or LOAEL	= 	Systemic toxicity level where no observed adverse effects (NOAEL) or where the lowest observed adverse effects (LOAEL) occurred in the study (mg ai/kg body weight/day); and

ADD 			= 	Average daily inhalation or dermal dose in a given scenario (mg ai/kg body weight/day).

In addition to the target MOEs presented in Table 3.2 that were used for the analysis, a series of assumptions and exposure factors served as the basis for completing the handler risk assessment. Each general assumption and factor for both residential and occupational assessments is detailed below.  Assumptions specific to the use site category are listed in each separate section of this document.  The general assumptions and factors include:

- Triclosan products are widely used and have a large number of use patterns that are difficult to completely capture in this document.  As such, EPA has patterned this risk assessment on a series of likely representative scenarios for each use site that are believed by EPA to represent the vast majority of triclosan uses.

- Based on the adverse effects for the endpoints, the body weight of 70 kg is used for the dermal and oral routes of exposure.

- Exposure factors used to calculate daily exposures to handlers were based on applicable data, if available.  When appropriate data were lacking, values from a scenario deemed similar were used.

- The maximum application rates allowed by labels were assumed.

## Chemical Identification

## Triclosan (5-Chloro-2-(2,4-dichlorophenoxy)phenol) was first registered with the EPA on June 19, 1969.  Triclosan is a diphenyl ether derivative.  The CAS number is 3380-34-5 and the molecular structure is provided in Figure 1.

Figure 1.  Molecular Structure of Triclosan

## 1.4	Physical/Chemical Properties

Table 1.2 shows physical/chemical characteristics that have been reported for triclosan.

| Table 1.2. Physical/Chemical Properties of Triclosan |
| --- |
| Parameter | Triclosan |
| Molecular Weight | 290 |
| Density | 1.55E3 kg/m3 at 22 ˚C |
| Boiling Point | Solid |
| Water Solubility | 12 ppm |
| Vapor Pressure | 5.2E-6 mm Hg at 25 ˚C |

# 2.0	 USE INFORMATION

## 2.1	 Formulation Types and Percent Active Ingredient

Triclosan is used as a bacteriostat, fungistat, mildewstat, and deodorizer. The products containing triclosan as the active ingredient (a.i) are formulated as ready-to-use, pelleted/tableted, emulsifiable concentrate, soluble concentrate, and impregnated materials. Concentrations of triclosan in these products range widely from 0.69% to ≥99%.

## 2.2	 Summary of Use Pattern and Formulations

The Agency determines potential exposures to handlers of the product by identifying exposure scenarios from the various application methods that are plausible, given the label uses.  Based on a review of product labels, triclosan is the active ingredient in products used in the following Use Site Categories:

- (III) Commercial, institutional and industrial premises and equipment,

- (IV) Residential and public access premises, and

- (VII) Material preservatives,

Specific uses within these use categories are identified in Table 2.1.  Examples of EPA registered uses for triclosan include application to textiles, plastics, paints, etc.  FDA uses of triclosan such as in hand soaps and toothpaste are out of the scope of this chapter but are used in the aggregate risk assessment.  From Table 2.1, EPA has selected representative exposure scenarios to assess triclosan in this document.  These scenarios were selected to be representative of the vast majority of uses and are believed to provide high-end degrees of dermal, inhalation, or incidental ingestion exposure.  The representative scenarios assessed in this document are shown in Table 4.1 (residential) and Table 6.1 (occupational).

| Table 2.1. Potential Use Scenarios Based on Product Labels for Triclosan. |
| --- |
| Use Site Category | Example Use Sites | Scenarios |
| Use Site Category III Commercial/ Institutional/Industrial | Conveyor belts, fire hoses, dye bath vats, ice making equipment, HVAC coils | Application to HVAC coils Painting (commercial painters) |
| Use Site Category IV Residential and Public Access Premises | Used as an end-use product in carpet shampoos (also used in treated articles) | Painting Exposure to treated articles (e.g., clothing, mattress, plastic toys) |
| Use Site Category VII Material Preservatives | Used in the production of various household, institutional and industrial items | adhesives paints (latex) textiles (cotton, wool, nylon, rayon, linen, fiber filling, mattress ticking) polymers and plastics |

# 3.0	SUMMARY OF TOXICITY DATA

## 3.1	Acute Toxicity

The acute toxicity data for triclosan are summarized below in Table 3.1 (USEPA, 2007).

| Table 3.1. Acute Toxicity Profile for Triclosan |
| --- |
| Guideline Number | Study Type/ Test substance (% a.i.) | MRID Number/ Citation | Results | Toxicity Category |
| 870.1100 (§81-1) | Acute Oral- Rat Triclosan (99.7% a.i.) | 43206501 | LD50: >5000 mg/kg | IV |
| 870.1200 (§81-2) | Acute Dermal- Rabbit Triclosan (97% a.i.) | 42306902 Phase III summary 92084037 | LD50: >9300 mg/kg | IV |
| 870.1300 (§81-3) | Acute Inhalation- Rat Triclosan (100.5% a.i.) | 42306902, 43310501 | LC50: >0.15 mg/L | II |
| 870.2400 (§81-4) | Primary Eye Irritation- Rabbit Triclosan (97% a.i.) | Phase III summary 92084040 | PIS: 92/110 (24 hours), 82/110 (72 hours) | II |
| 870.2500 (§81-5) | Primary Dermal Irritation- Rabbit Triclosan (% a.i.not provided) | 42306903 | PII: 3.5 at 72 hours | III |
| 870.2600 (§81-6) | Dermal Sensitization- Guinea Pig Triclosan (99.7% a.i.) | 43206502 | Not a Sensitizer | NA |

## 3.2	Summary of Toxicity Endpoints

Table 3.2 summarizes the toxicological endpoints for Triclosan (USEPA, 2007).

Table 3.2.  Summary of Toxicological Dose and Endpoint Selection for Triclosan.

| Exposure Scenario | Dose Used in Risk Assessment, UF | Special FQPA SF* and Level of Concern for Risk Assessment | Study and Toxicological Effects |
| --- | --- | --- | --- |
| Acute Dietary (gen. pop.) | NOAEL = 30 mg/kg UF = 100 | FQPA SF = 1x | Chronic Toxicity study in Baboons MRID 257773. Effects of clinical signs of toxicity include vomiting, failure to eat, and diarrhea. |
| Acute Dietary (females 13+) | Endpoint not identified in the database |
| Chronic Dietary (all populations) | NOAEL = 30 mg/kg UF = 100 | FQPA SF = 1x | Chronic Toxicity study in Baboons MRID 257773. Effects of clinical signs of toxicity include vomiting, failure to eat, and diarrhea. |
| Short-Term/ Intermediate-Term Incidental Oral (1-30 days; 30 days- 6 months) | NOAEL = 30 mg/kg UF = 100 | FQPA SF = 1x | Chronic Toxicity study in Baboons MRID 257773 Effects of clinical signs of toxicity include vomiting, failure to eat, and diarrhea. |
| Dermal (short-term) | NOAEL = 0.6 mg/animal @ 99.3% active ingredient (100 µg/cm2) UF = 10x | FQPA SF = 1x | 14-day dermal toxicity study in the mouse MRID 44389708 LOAEL = 1.5 mg/kg/day, based on treatment-related dermal irritation at the treatment site and on increased liver weights |
| Dermal (intermediate term) | NOAEL = 40 mg/kg UF = 100 | FQPA SF = 1x | 90-day dermal toxicity study in rats. MRID 43328001. LOAEL = 80 mg/kg/day, based on increased incidence occult blood in the urine. |
| Dermal (long-term) | NOAEL = 40 mg/kg UF = 300 | FQPA SF = 1x | 90-day dermal toxicity study in rats. MRID 43328001. LOAEL = 80 mg/kg/day, based on increased incidence occult blood in the urine. |
| Inhalation (all durations) | LOAEL = 50 mg/m3 or 3.21 mg/kg/day UF = 1000 Where mg/kg/day = ((0.0087 m3/hr * mg/m3 * 2 hr/day) /0.271 b.w. | FQPA SF = 1x | 21-Day Inhalation Toxicity study in the rat. MRID 0087996. Effects seen in males at LOAEL include increased total leucocyte count and increased serum alkaline phosphatase. |
| Cancer (oral) | Not likely to be carcinogenic to humans (Health Effects Division Carcinogencity Assessment Review Committee, July 2007). |

UF = uncertainty factor, FQPA SF = Special FQPA safety factor, NOAEL = no observed adverse effect level, LOAEL = lowest observed adverse effect level, PAD = population adjusted dose (a = acute, c = chronic) RfD = reference dose, MOE = margin of exposure, LOC = level of concern, NA = Not Applicable

## 3.3	FQPA Considerations

The hazard-based FQPA factor should be removed because the toxicology data provided no indication of increased susceptibility of rats or rabbits to in utero and/or postnatal exposure to triclosan and there is no evidence of developmental anomalies, including abnormalities in the development of the fetal nervous system, in the pre- and/or post-natal studies.  Additionally, there are no data gaps for evaluation of increased susceptibility to infants and children.

# 4.0	RESIDENTIAL EXPOSURE ASSESSMENT

## 4.1	Summary of Registered Uses

There are no EPA registered products containing triclosan that can be applied directly by the homeowner.  There is a homeowner application of triclosan when it is used as an in-can preservative for latex paint (e.g., EPA Reg. No. 42182-1).  Articles treated with triclosan as a bacteriostat in occupational settings (e.g., EPA Reg. No. 70404-5) may also have the potential for post-application residential exposure.  Triclosan-treated articles that may routinely be used in the residential market include, but are not limited to, material preservative uses in mattresses, clothing, tooth brush bristles, plastic toys, garbage bags, paper, playground equipment, sponges, furniture, footwear, etc.  Additionally, triclosan can be used to control/prevent/inhibit the growth of fungi/mildew/mold/bacteria on coils in residential heating, ventilating, and air conditioning (HVAC) systems (e.g., EPA Reg. No. 82523-1).  HVAC coil applications of triclosan are restricted to service contractors only.  There are no homeowner applications to HVAC coils.

## 4.2	Residential Exposure

The exposure scenarios assessed in this document for the representative uses of triclosan selected by EPA are listed in Table 4.1. The table also shows the maximum application rate associated with the representative use and the EPA Registration number for the corresponding product label(s).  It should be noted that for the calculation of application rates in which 8.34 lb/gal is noted, the product is assumed to have the density of water because no product-specific density is available. Handler dermal and inhalation exposures are assessed for the carpet shampoo and for the in-can preservative use in paint.  Post-application dermal, inhalation, and/or incidental ingestion exposures are assessed for treated articles including mattresses and clothing.  Post-application/bystander inhalation exposures are expected to be minimal for most uses because of the low vapor pressure and non spray uses, except for the painting and HVAC coil uses.  The inhalation bystander exposure to aerosols generated during painting are assumed to be less then that of the applicator and are therefore not assessed separately.  The HVAC coil applications are not expected to result in post-application inhalation exposures because of the low vapor pressure of triclosan and the HVAC treatment is limited to coils, not duct work.

| Table 4.1. Representative Uses Associated with Residential Exposure to Triclosan. |
| --- |
| Representative Use | Application Method | Exposure Scenario | Example Registration Number | Application Rate |
| Paint (Latex) | Brush and airless sprayer | ST Handler: adult dermal and inhalation. | 42182-1 | 0.1 lb ai/gallon [up to 1% product x 99% ai x 10 lb/gal paint density = 0.099 lb ai/gallon of paint] |
| Textiles (exposures to treated articles are represented by exposure to mattress and clothing) | NAa | ST Post-app: wearing treated clothing, adult dermal; child incidental ingestion and dermal | 70404-5 | Round to 2% ai in finished textiles and mattresses. (Rates range up to the finished product containing 2% formulated product by weight. Triclosan product contains 99% ai. ) |
| Plastic (exposures to plastic treated articles are represented by plastic toys) | NAa | ST Post-app: child incidental ingestion and dermal | 42182-1 | 0.5% ai (0.1% to 0.5% product x 99% ai) Note: labels need to clarify that toys are limited to 0.5% |

(a ) The handlers scenarios were not assessed because the products can only be applied occupationally.

### 4.2.1	Residential Handler Exposures

The residential handler scenarios described in Table 4.1 were assessed to determine inhalation exposures.  Dermal exposures for the short-term duration were not assessed because no systemic dermal toxicity was observed.  Dermal irritation was observed in the toxicity study but for the 99% ai test substance.  Residential uses are at or below 1% ai or are impregnated into finished products.  The scenarios were assessed using PHED and CMA data and the equations in Section 1.2, “Criteria for Conducting Risk Assessment.”  A summary of the PHED and CMA data sets are presented in Appendix A.

Unit Exposure Values: Unit exposure values were taken from the PHED data presented in HED’s Residential SOPs (USEPA, 1997) and from the CMA data from the EPA memorandum Evaluation of Chemical Manufacturers Association Antimicrobial Exposure Assessment Study (USEPA, 1999).

- For the airless sprayer scenario, the PHED inhalation unit exposure value for a residential handler applying a pesticide using an airless sprayer was used.  The unit exposure value (0.83 mg/lb ai) represents a handler using an airless sprayer to stain the exterior of a house.

- For the brush/roller scenario, the PHED inhalation unit exposure value for a residential handler is based on applying a fungicide in paint to bathroom walls using a paint brush.  The unit exposure value is 0.28 mg/lb ai.

Quantity handled/treated: The quantities handled/treated were estimated based on information from various sources, including EPA estimates.

- For the brush/roller in paint applications, it is assumed that 20 lbs (approximately 2 gallons) of treated paint will be used.  This is based on the 90th percentile value of 8 gallons of latex paint used per year divided by the mean frequency of 4 painting events/year.

- For the airless sprayer in paint applications, it is assumed that 150 lbs           (approximately 15 gallons) of treated paint will be used.  This is based on the coverage of 200 ft2/gallon and a house size of 40 x 30 x 20 ft (surface area of 2,800 ft2).

Duration of Exposure: The duration of exposure for most handler homeowner uses is believed to be best represented by the short-term duration (1 to 30 days).  The reason that short-term duration was chosen to be assessed is because painting is episodic in nature, not daily.  In addition, homeowners are assumed to use different products with varying activities, not exclusively triclosan treated products (e.g., in-can paint preservative).

Results

The resulting short-term inhalation exposures and MOEs for the representative residential handler scenarios are presented in Table 4.2.  The short-term dermal endpoint is based on dermal irritation effects when a 99 percent active ingredient was applied for 14-days to a mouse. Because the products applied by homeowners are equal to or less then 1 percent, a short-term dermal assessment was not deemed appropriate (i.e., even at the exaggerated concentration in the toxicity study the MOEs would not be of concern).  The calculated inhalation MOEs are above the target MOE of 1000 for the paint brush but below the target MOE for the airless sprayer (i.e., MOE = 180).  Therefore, the risk exceeds EPA’s level of concern for painting.  Personal protective equipment (PPE) such as respirators is not a viable option for residential uses.

| Table 4.2 Triclosan Short-Term Residential Handler Inhalation Exposures and MOEs |
| --- |
| Exposure Scenario Application Method | Application Method | Application Ratea | Quantity Handled/ Treated per dayb | Unit Exposure (mg/lb a.i.) | Daily Dose (mg/kg/day) c | MOE d (Target MOE = 1000) |
| Painting | Paint brush | 0.1 lb ai/gal | 2 gallons | 0.28 | 0.0008 | 4,000 |
|  | Airless sprayer |  | 15 gallons | 0.83 | 0.018 | 180 |

a	Application rates are the maximum application rates determined from EPA registered labels for triclosan.

b	Amount handled per day values are estimates or label instructions.

c	Daily dose (mg/kg/day) = [unit exposure (mg/lb a.i.) x application rate (% a.i. weight or lb ai/gal) x quantity treated (lb/day or gal/day) x absorption factor (1.0 for inhalation)]/ Body weight (70 kg for inhalation).

d	MOE = LOAEL / Daily Dose.  [Where short-term inhalation LOAEL = 50 mg/m3 or a dose of 3.21 mg/kg/day]. Target MOE = 1000.

### 4.2.2	Residential Post-application Exposures

For the purposes of this screening-level assessment, post-application scenarios have been developed that encompass multiple products, but still represent a high end exposure scenario for all products represented. As shown in Table 4.1, representative post-application scenarios assessed include wearing treated clothing (dermal intermediate-term exposure to adults and children and incidental oral exposure to children) and children playing with treated plastic toys (incidental oral exposure).  The short-term dermal duration was not assessed because no systemic toxicity was observed.  However, systemic toxicity was observed for the intermediate-term oral endpoint and this endpoint was selected to assess the dermal route of exposure.

#### 4.2.2.1		Textiles

#### Dermal Exposure to Adults and Toddlers from Contacting Treated Clothing

There is the potential for dermal exposure to adults and children from wearing clothing treated via factory impregnation of the chemical as a preservative.  A post-application assessment assuming no laundering was conducted as a conservative measure (i.e., the effect on dislodgeable residues over time during washing is not quantifiable).  It should be noted that not all articles of clothing are treated with triclosan products or worn on a continuous basis.  In general, it is believed that most treated textiles used in a residential setting will result in exposures occurring over a short-term time duration (1 to 30 days) because residents are assumed to be exposed to treated textiles with varying active ingredients, not exclusively triclosan treated textiles.  However, both the short- and intermediate-term exposure durations are assessed for the clothing scenarios as this scenario is being used to represent all textile uses that may occur over time (e.g., pillow cases, mattresses, footwear, etc) where daily exposure may occur.  Long-term duration was not assessed because dislodgeable triclosan residues are not expected to be available continuously.

Exposure Calculations

Potential doses are calculated as follows:

PDD = W x % applied x % a.i. x % transfer

BW

where:

PDD		= 	potential daily dose (mg/kg/day);

W 		= 	weight of clothing worn (g/day);

% applied	= 	percent of product applied (%);

% a.i.		= 	percent active ingredient in product (%);

% transfer	= 	percent transferred (%); and

BW		=	body weight (kg).

And

W = (SW/SSA) * BSA

where:

W	=	weight of clothing worn (g/day);

SW 	=	weight of medium shirt (g);

SSA 	= 	surface area of medium shirt (cm2); and

BSA	=	surface area of body covered (cm2).

Assumptions

- The product is applied at rates as high as 2% of weight of textile; the highest application rate of 2% product corresponds with the highest percent triclosan formulation (i.e., 99 percent active ingredient, EPA Reg. No. 70404-5).

- The median surface area of clothing contacting skin for a 3-year-old toddler is 5,670 cm2 (total body surface area minus the head) (USEPA, 1997).  For adults, the median surface area is 16,900 cm2 (total body surface area minus the head) (USEPA, 1997).  Note:  The Phase I comments suggested that triclosan in textiles is primarily limited to sports wear.  However, no refinements to the assessment have been made to represent short pants and short-sleeved shirts because it is not a label restriction and some sports wear may be long pants and long-sleeved shirts (e.g., sweat pants and sweat shirts).

- The textile density is 10 mg/cm2 based on the density of mixed cotton and synthetics (HERA 2003).  It is assumed that the mixed cotton/synthetic is used to cover the body for both adults and toddlers, minus the head surface area.  Therefore, the total amount of fabric worn per day is equal to the density of the fabric (10 mg or 0.01 grams per cm2) times the surface area covered (5,670 cm2 for toddlers, 16,900 cm2 for adults), or 56.7 g/day for toddlers, and 169 g/day for adults.  Note:  Phase I comments suggested that the surface area should be adjusted for inside surface area of clothing contacting skin (i.e., 50% adjustment).  However, adjustments were not made to the assessment because the transfer of triclosan residues may come from both dermal contact with the suggested inside surface of clothing as well as sweat-soaked clothing which would appear to include the full fabric.  Adjustments were also suggested for the fact that clothing is only worn 12 hours per day and triclosan represents less than 100% market share.  These adjustments were not made for this screening-level single textile use because insufficient information on residue transfer to a person’s skin over time is not available and risks are determined for those individuals wearing the treated clothing articles (i.e., not a population adjusted risk assessment).  However, the aggregate assessment using the NHANES biological monitoring data for triclosan is based on real world exposures and is believed to be the best data available to regulate the uses.  The aggregate assessment is presented in the triclosan risk assessment chapter supporting the triclosan RED document.

- Potential doses were calculated using residue transfer factor of 0.55% from a leaching study developed by Sanitized, Inc, dated December 4, 2007.  The leaching study provided results for cotton (0.55% leached), wool (0.06% leached), and two poly-based fabrics (0.00% for PA and 0.34% for PES).  The cotton fabric leached the highest amount over a 48 hour period at 20 degrees C.  The study used an acidic sweat solution at a pH of 5.5 and the ISO 105/E04 method to extract the triclosan from the various treated fabrics.

- Toddlers (3 years old) are assumed to weigh 15 kg. This is the mean of the median values for male and female toddlers (USEPA, 1997).  For adults, a body weight of 70 kg has been assumed. (USEPA, 1997).

Results

The calculations of the intermediate-term dermal doses and MOEs for adults and toddlers wearing treated clothing are shown in Table 4.5.  The dermal MOEs for adults and toddlers are equal to or above the target MOE of 100.

At this point in time, triclosan-treated mattresses are not assessed separately but are not of concern as they are treated at the same concentration as the textiles/clothing.

| Table 4.5: Dermal Intermediate-term Post-application Exposures and MOEs for Toddlers and Adults Contacting Treated Clothing |
| --- |
| Exposure Scenario | Weight of clothing worn (g/day)a | Percent triclosan in product (%) | Percent of product applied (%) | Percent residue transferred from clothing to skin (%) | Daily doseb (mg a.i./ kg/day) | Dermal MOEc (Target MOE=100) |
| Toddler | 56.7 | 99% | 2% | 0.55 % | 0.41 | 98 |
| Adult | 169 | 99% | 2% | 0.55% | 0.26 | 150 |

a.	Weight of clothing worn (g/day) = (Density of fabric 0.01 g/cm2) * (surface area of body covered, cm2) * 1 outfit/day

b.	Daily Dose (mg/kg/day) = [(weight of clothing worn, g/day) * (percent a.i. in product, %) / 100 * (percent of product applied, %) / 100 * (percent residue transferred from clothing to skin, %/100) * (dermal absorption factor, 1) * (conversion factor, 1000 mg/g)] / (body weight, 15 and 70 kg).

c. 	Dermal MOE = NOAEL (mg/kg/day) / Daily Dose [Where intermediate-term dermal NOAEL = 40 mg/kg/day].  Target MOE = 100.

#### Incidental Oral Exposure to Toddlers Mouthing Treated Textiles (Clothing/Blankets)

Exposure Calculations

There is the potential for incidental oral exposure to toddlers from mouthing textiles treated with triclosan.

Potential doses are calculated as follows:

PDD = C x SE x SA

BW

where:

PDD	= 	potential daily dose (mg/kg/day);

C 	= 	concentration on clothing (mg/cm2);

SE	=	saliva extraction efficiency (%);

SA 	= 	surface area mouthed (cm2/day); and

BW 	= 	body weight (kg).

And

C = % a.i. x % applied x W x CF1 x CF2

where:

C		=	concentration on clothing (mg/cm2);

% applied	= 	percent of product applied (%);

% a.i.		= 	percent active ingredient in product (%);

W 		= 	weight of clothing (g/m2);

CF1		=	unit conversion factor (1,000 mg/g); and

CF2		=	unit conversion factor (0.0001 m2/cm2).

Assumptions

- The product is applied at a maximum label rate of 2% of weight of textile; the percent of triclosan in the formulation is 99%.  A reduction of the application rate to 0.99% by weight is also included as an indicator of reduced risk.

- The textile density is 10 mg/cm2 (0.01 grams/cm2 or 100 grams/m2) based on the density of mixed cotton and synthetics (HERA 2003).

- The leaching study for triclosan (see dermal scenario above) provided a value of 0.55% leaching from cotton fabric.  However, the results from leaching studies may underestimate the amount of residue transfer for mouthing clothing because of the mouthing/sucking action of a child may be more vigorous then leaching.  Nonetheless, the leaching study (conducted for 48 hours) is believed to be more representative for triclosan then the default value typically used for saliva extraction.  The magnitude of the resulting MOE estimate should be sufficient based on the use of the 48-hour leaching results versus a mouthing/sucking action.  More research on residue transfer from mouthing is warranted.

- The surface area of textiles mouthed by toddlers is 100 cm2, a 4 inch x 4 inch area (professional judgment).

- Toddlers (3 years old) are used to represent the 1 to 6 year old age group.  For three-year olds, the median body weight is 15 kg (USEPA, 1997).

Results

Table 4.6 shows the calculation of the short- and intermediate-term oral dose and oral MOE for toddlers mouthing treated textiles. The MOE value is above the target MOE of 100 for the maximum concentration allowed on the label (MOE = 4,200).

At this point in time, triclosan treated mattresses are not assessed separately but are not of concern as they are treated at the same concentration as the textiles/clothing.

| Table 4.6: Incidental Oral Exposures and MOEs for Toddlers Wearing Treated Textiles (Clothing/Blankets) |
| --- |
| Weight of clothing (g/cm2) | % Product Applied | Concentration on clothinga (mg/cm2) | Surface area mouthed (cm2/day) | Saliva extraction efficiency (%) | Potential daily dose (mg a.i./kg/day) | Incidental Oral MOEc (Target MOE =100) |
| 0.01 | 2% | 0.198 | 100 | 0.55% | 0.0073 | 4,200 |

a.	Concentration on clothing (mg/cm2) = (percent a.i. in product, %) / 100 * (percent product applied, %) / 100 * (weight of clothing, g/cm2) * 1,000 mg/g

b.	Potential Daily Dose (mg/kg/day) = (concentration on clothing, mg/cm2) * (surface area mouthed, cm2/day) * (saliva extraction efficiency, %)/100 / (body weight, 15 kg).

c 	Oral MOE = NOAEL (mg/kg/day) / Potential Daily Dose [Where short- and intermediate-term incidental oral NOAEL = 30 mg/kg/day].  Target MOE = 100.

4.2.2.2		Plastics (Toys)

Plastics and polymers used in toys can be treated with triclosan during the manufacturing process.  Therefore children’s post application incidental oral exposures to treated toys may occur.  It was assumed that not all plastic toys are treated with triclosan and the toys that are treated will not be used everyday therefore exposure would occur intermittently.  Thus only short-term exposures durations were assessed.

Child Incidental Ingestion Exposure from Treated Plastic

Exposure Calculations

Short-term exposures – There is potential for short- term incidental ingestion exposures when children come into mouth plastic toys treated with triclosan.  To determine short-term exposure of children to triclosan in plastic toys, the following equations were used:

# PDD = SR x SE x SA

# BW

where:

PDD	= 	potential daily dose (mg/kg/day);

SR 	= 	surface residue (mg/cm2);

SE	=	saliva extraction efficiency (unitless fraction)

SA	=	surface area of toy mouthed (cm2/day)

BW 	= 	body weight of a toddler (kg).

# And

# SR = % a.i x W x CF x F

# SA

where:

SR	=	surface residue (mg a.i./cm2)

% a.i.	=	fraction active ingredient in toy by total weight (unitless)

W	=	weight of toy (g)

CF	=	conversion factor (1,000 mg/g)

F	=	fraction additive available at the surface of the toy (unitless)

SA	=	surface area of toy (cm2)

Assumptions

- It is assumed that 500 cm2 is a representative surface area of plastic that is mouthed (AD standard assumption).

- Since chemical specific leaching data were not available, the actual amount of active ingredient at the surface of the toy which is available for mouthing is based on the following assumptions

  - The toy is manufactured from ABS or polystyrene plastic;

  - The diffusion of the active ingredient available at the surface of the toy to the child’s mouth is allowed to reach equilibrium; and

  - No more than 0.5% of the additive is available on the surface of the toy for each mouthing event.

- The weight of a 500 cm2 toy is 50 g, which is based on data showing that a polyethylene highchair sample with a surface area of 12.7 cm2 weighs 1.3072 g (i.e., 0.1 g/cm2) (AD standard assumption).

- The product contains 99% a.i. by weight and is used in plastic at a rate of 0.5% product by weight of material; thus, the % a.i. in plastic is 99% ai x 0.5% = 0.5% ai.

- The saliva extraction efficiency is assumed to be 50% (EPA 2001).

- The body weight of a child was assumed to be 15 kg.

Results

Table 4.12 shows the calculations of the short-term incidental oral exposure and MOE for children mouthing treated plastic toys.  The ST MOE is above the target MOE of 100 and is not of concern.

| Table 4.12. Short-term Incidental Oral Exposure and MOE for Children Mouthing Treated Plastic Toys |
| --- |
| Duration | % a.i. | Plastic Weight (g) | Fraction of triclosan available on plastic surface | Surface area mouthed (cm2) | Residue on Surface of plastic (mg/cm2) | Saliva extraction efficiency | Exposure a (mg/kg/day) | MOE (Target MOE is 100) b |
| ST | 0.5% | 50 | 0.5% | 500 | 0.0025 | 50% | 0.042 | 710 |

ST = short-term duration (1 to 30 days)

(a )  Potential exposures are expressed as mg/kg/day; equations used to estimate exposure are presented above.

(b)  MOE = NOAEL/exposure estimate [Where: ST incidental oral NOAEL = 30 mg/kg/day].  Target MOE = 100.

4.2.3	Data Limitations/Uncertainties

There are several data limitations and uncertainties associated with the residential handler and post-application exposure assessments.  These include the following:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix A for summaries of these data sources). Most of the CMA data are of poor quality, therefore, EPA requires that confirmatory monitoring data be generated to support the values used in these assessments.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA, 2000 and 2001).  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on AD estimates and could be further refined from input from registrants.

# RESIDENTIAL AGGREGATE RISK ASSESSMENT AND CHARACTERIZATION

Residential aggregate exposure and risk assessment is addressed within the preliminary risk assessment chapter.  Based on a review of EPA product labels, triclosan is the active ingredient in products used in paints, textiles (mattresses and clothing) and plastic toys,  Exposures also include  those uses where there is the  possibility of indirect food migration, including  paper/pulp use,  use in ice-making equipment, adhesives, cutting boards, and counter tops  as well use in conveyer belts. In addition to EPA-regulated uses, the aggregate assessment accounts for non-EPA regulated uses of triclosan.  Non-EPA uses include FDA uses such as toothpaste, hand soaps, and deodorants.

Although individual EPA-regulated uses have been assessed in this chapter using standard Agency methodology, the NHANES biological monitoring data are available for assessing aggregate exposure and risk.  EPA views the NHANES data as more representative of aggregate exposures than determining probability of co-occurrence of EPA and FDA-regulated uses.

# 6.0	OCCUPATIONAL EXPOSURE ASSESSMENT

The exposure scenarios assessed in this document for the representative uses selected by EPA are shown in Table 6.1. The table also shows the maximum application rate associated with the representative use and the appropriate EPA Registration number for the product label.  It should be noted that for the calculation of application rates in which 8.34 lb/gal is noted, the product is assumed to have the density of water because no product-specific density is available.

Potential occupational handler exposure for triclosan can occur in three use sites:   commercial/institutional/industrial premises and equipment, material preservatives, and industrial processes and water systems.

| Table 6.1. Representative Exposure Scenarios Associated with Occupational Exposures to Triclosan |
| --- |
| Representative Use | Method of Application | Exposure Scenario | Example Registration # | Application Rate |
| Commercial/Industrial/Institutional Premises (Use Category III) |
| HVAC coil applications | Airless sprayer | ST/IT Handler: Inhalation | 82523-1 | 6.1E-4 lb ai/10 ft2 (0.85 pints/10 ft2 x 1 gal/8 pts x 8.34 lb/gal x 0.69% ai) |
| Painting (commercial painters) | Paint brush, Airless sprayer | ST/IT Handler: Inhalation | 42182-1 | 0.1 lb ai/gallon [up to 1% product x 99% ai x 10 lb/gal paint density = 0.099 lb ai/gallon of paint] |
| Material Preservatives (Use Category VII) |
| Paint | Liquid pour, Powder | ST/IT Handler: inhalation | 42182-1 | 0.1 lb ai/gallon [up to 1% product x 99% ai x 10 lb/gal paint density = 0.099 lb ai/gallon of paint] |
| Industrial processes and water systems (Use Category VIII) |
| Pulp and Paper | Metered pump | ST/IT Handler: Inhalation | 70404-5 | 2% ai by weight of paper product (2% product by weight x 99% ai for paper mulch ) Note : other labels for paper and paper board have lower rates, 42182-1 and 3090-165) |

## 6.1 	Occupational Handler Exposures

The occupational handler scenarios included in Table 6.1 were assessed to determine inhalation and dermal exposures.  The general assumptions and equations that were used to calculate occupational handler inhalation risks are provided in Section 1.2, Criteria for Conducting the Risk Assessment. The majority of the scenarios were assessed using CMA data and Equations 1-3 as outlined in Section 1.2.  However, for the occupational scenarios in which CMA data were insufficient, other data and methods were applied.

Triclosan short-term dermal irritation exposures and risks were not estimated for occupational handler exposures.  Instead, dermal irritation exposures and risks will be mitigated using default personal protective equipment requirements based on the toxicity of the end-use product.  The systemic dermal assessment is based on a dermal route-specific endpoint, and therefore, dermal absorption adjustments are not necessary.  The intermediate- and long-term dermal endpoints are identical (but require different target MOEs to account for the long-term duration).

Unit Exposure Values (UE):  Inhalation and dermal unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999b: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998).

- The For the liquid pour scenarios, the unit exposure depends on the material being treated. The following CMA unit exposures were available and used for the assessment of the risk associated with the treatment of the specified materials.

  - Paint manufacturing: CMA preservative data.  The dermal unit exposure is 0.135 mg/lb ai (gloved).  The inhalation unit exposure is 0.00346 mg/lb a.i.  These unit exposure values are based on 2 replicates where the test subjects were wearing a single layer of clothing and chemical resistant gloves. Although these unit exposures are based on minimal replicates, the exposure values are similar to the ones found in PHED for a similar scenario.

The For the liquid/metering pump scenarios, the unit exposure depends on the material being treated. The following CMA unit exposures were available and used for the assessment of the risk associated with the treatment of the specified materials.

  - Paint and pulp & paper:  CMA preservative pump data.  The dermal UE is 0.00629 mg/lb ai(with gloves) and the inhalation UE is 0.000403 mg/lb ai.  The values are based on two replicates where the test subjects were wearing a single layer of clothing and chemical resistant gloves.

- For airless sprayer scenarios, the occupational PHED inhalation and dermal unit exposure values for airless sprayer application (PHED scenario 23) were used. The inhalation exposure value is 0.83 mg/lb ai.  The dermal unit exposure is 38 mg/lb ai for ungloved replicates. PPE are not considered for material preservatives in paint because the paint is considered a treated article and as such there is no pesticide label on the paint container to communicate PPE.

- For roller/brush scenarios, the occupational PHED dermal and inhalation unit exposure values for paintbrush applications (PHED scenario 22) were used (single layer of clothing).  The inhalation exposure value is 0.28 mg/lb a.i. The dermal unit exposure is 180 mg/lb ai for no glove replicates.  PPE are not considered for material preservatives in paint because the paint is considered a treated article and as such there is no pesticide label on the paint container to communicate PPE.

Quantity handled/treated: The quantity handled/treated values were estimated based on information from various sources.  The following assumptions were made:

- For the liquid pour scenarios, the quantity of the chemical that is handled depends on the material that is being treated.  The following values were used for the different materials:

  - Paint:  20,000 lbs (approximately 2,000 gallons, weight based on a density 10 lb a.i./gal) (standard AD assumption).

For the liquid/metering pump scenarios the quantity that is handled depends on the material that is being treated.  The following values were used for the different materials:

  - Pulp and Paper:  500 tons/day.

  - Paint:  200,000 lbs (approximately 20,000 gallons, weight based on a density of 10 lb a.i./gal) (standard AD assumption).

- For the roller/brush painting scenario, it was assumed that 50 lbs (approximately 5 gallons of paint with a density of 10 lb/gal) of treated paint are used (standard AD assumption).

- For the airless sprayer in the painting scenario, it was assumed that 500 lbs (approximately 50 gallons of paint with a density of 10 lb/gal) of treated paint are used. (standard AD assumption).

- For the airless sprayer in the HVAC coil scenario, it was assumed 1,000 ft2 of coil surface area is treated.

Duration of Exposure: The MOEs were calculated for the short- and intermediate-term durations for occupational handlers using the appropriate endpoints in Table 3.2.

Exposure Calculations and Results

The resulting inhalation and dermal exposures and MOEs for the representative occupational handler scenarios are presented in Table 6.2. The calculated dermal MOEs were above the target MOE of 100 for all scenarios, except for the commercial painters (both by brush and airless sprayer) and the pulp & paper use.  The inhalation MOEs are below the target MOE of 1000 for the airless sprayer (paint), the paint manufacturing, and the pulp and paper.

| Table 6.2. Short- and Intermediate-Term Inhalation Risks Associated with Occupational Handlers |
| --- |
| Exposure Scenario | Method of Application | Unit Exposure (mg/lb a.i.) | Application Rate | Quantity Handled/ Treated per day | Daily Dose (mg/kg/day)a | MOEb (Target MOEs = 1000 inhalation, 100 dermal) |
|  |  | Inhalation | Dermal |  |  | Inhalation | Dermal | Inhalation | Dermal |
| Commercial, Institutional and Industrial Premises and Equipment (Use Site Category III ) |
| HVAC | Airless sprayer | 0.83 | 38 | 6.1E-4 lb ai/10ft2 | Large building 1000 ft2 | 0.00072 | 0.033 | 4,500 | 1,200 |
| Painting (commercial) | Paint brush | 0.26 | 180 | 0.1 lb ai/gal | 5 gallons | 0.002 | 1.3 | 1,600 | 31 |
|  | Airless sprayer | 0.83 | 38 |  | 50 gallons | 0.059 | 2.7 | 54 | 1 |
| Material Preservatives (Use Site Category VII) |
| Paint (manufacturing process) | Liquid pour | 0.00346 | 0.135 (gloves) | 0.99% ai | 20,000 lbs | 0.0098 | 0.38 | 330 | 110 |
|  | Liquid pump | 0.000403 | 0.00629 (gloves) |  | 200,000 lbs | 0.011 | 0.18 | 290 | 220 |
| Industrial Processes and Water Systems (Use Site Category VIII) |
| Pulp and Paper | Metering pump | 0.000403 | 0.00629 (gloves) | 2% ai | 500 tons | 0.115 | 1.8 | 28 | 22 |

a	Daily dose (mg/kg/day) = [unit exposure (mg/lb a.i.) x absorption factor (1 for inhalation and 1 for dermal) x application rate x quantity treated / Body weight (70 kg).

b	MOE = LOAEL or NOAEL  (mg/kg/day) / Daily Dose [Where inhalation LOAEL = 3.21 mg/kg/day for all inhalation exposure durations and the IT dermal NOAEL is 40 mg/kg/day from a dermal route-specific study].  Target MOE = 1000 for inhalation and 100 for dermal.

## 6.2  	Occupational Post-application Exposures

Occupational post-application dermal and inhalation exposures are assumed to be negligible based on the use patterns.

## 6.3	Data Limitations/Uncertainties

There are several data limitations and uncertainties associated with the occupational handler and post application exposure assessments.  These include:

- Surrogate dermal and inhalation unit exposure values were taken from the proprietary Chemical Manufacturers Association (CMA) antimicrobial exposure study (USEPA, 1999: DP Barcode D247642) or from the Pesticide Handler Exposure Database (USEPA, 1998) (See Appendix A for summaries of these data sources).   Since the CMA data are of poor quality, the Agency requires that confirmatory data be submitted to support the occupational scenarios assessed in this document.

- The quantities handled/treated were estimated based on information from various sources, including HED’s Standard Operating Procedures (SOPs) for Residential Exposure Assessments (USEPA, 2000 and 2001), and personal communication with experts.  The individuals contacted have experience in these operations and their estimates are believed to be the best available without undertaking a statistical survey of the uses.  In certain cases, no standard values were available for some scenarios.  Assumptions for these scenarios were based on AD estimates and could be further refined from input from registrants.

# 7.0	REFERENCES

DOE.  1997.  Energy Information Administration: Profile of Commercial Buildings in 1995.  http://www.eia.doe.gov/emeu/cbecs/char95/profile.html

Freeman, N , Jimenez M, Reed KJ,Gurunathan S, Edwards RD, Roy A, Adgate JL, Pellizzari ED, Quackenboss J, Sexton K, Lioy PJ, 2001.  Quantitative analysis of chilren’s microactivity patterns:  The Minnesota Children’s Pesticide Exposure Study.  Journal of Exposure Analysis and Environmental Epidemiology.  11(6): 501-509.

USEPA. 1996.  Office of Research and Development, Descriptive Statistics Tables from a Detailed Analysis of the National Human Activity Pattern (NHAPS) Data; EPA/600/R-96/148, July 1996.   Data Collection Period October 1992 - September 1994 .

USEPA.  1997.  Exposure Factors Handbook. Volume I-II.  Office of Research and Development.  Washington, D.C.  EPA/600/P-95/002Fa. August 1997.

USEPA. 1998. PHED Surrogate Exposure Guide. Estimates of Worker Exposure from the Pesticide Handler Exposure Database Version 1.1.   Washington, DC:  U.S. Environmental Protection Agency.

USEPA. 1999.  Evaluation of Chemical Manufacturers Association Antimicrobial Exposure Assessment Study (Amended on 8 December 1992).  Memorandum from Siroos Mostaghimi, PH.D., USEPA to Julie Fairfax, USEPA. Dated November, 4 1999.  DP Barcode D247642.

USEPA.  2000.  Residential SOPs.  EPA Office of Pesticide Programs, Human Health Effects Division. Dated April 5, 2000.

USEPA.  2001.  HED Science Advisory Council for Exposure. Policy Update, November 12.  Recommended Revisions to the Standard Operating Procedures (SOPs) for Residential Exposure Assessment, February 22, 2001.

USEPA.  2007.  5-Chloro-2-(2,4-dichlorophenoxy)phenol (triclosan): Toxicology Chapter for the Reregistration Eligibility Decision (RED) document.

# APPENDIX A: Summary of CMA and PHED Data

Chemical Manufacturers Association (CMA) Data:

In response to an EPA Data Call-In Notice, a study was undertaken by the Institute of Agricultural Medicine and Occupational Health of The University of Iowa under contract to the Chemical Manufacturers Association.  In order to meet the requirements of Subdivision U of the Pesticide Assessment Guidelines (superseded by  Series 875.1000-875.1600 of the Pesticide Assessment Guidelines), handler exposure data are required from the chemical manufacturer specifically registering the antimicrobial pesticide.   The applicator exposure study must comply with the assessment guidelines for Applicator Exposure Monitoring in Subdivision U and the Occupational and Residential Exposure Test Guidelines in Series 875.  For this purpose, CMA submitted a study on 28 February, 1990, entitled "Antimicrobial Exposure Assessment Study (amended on December 8, 1992)" which was conducted by William Popendorf, et al.  It was evaluated and accepted by Occupational and Residential Exposure Branch (OREB) of Health Effect Division (HED), Office of Pesticides Program (OPP) of EPA in 1990.  The purpose of this CMA study was to characterize exposure to antimicrobial chemicals in order to support pesticide reregistrations (CMA, 1992).  The unit exposures presented in the most recent EPA evaluation of the CMA database (USEPA, 1999b) were used in this assessment.

The Agency determined that the CMA study had fulfilled the basic requirements of Subdivision U - Applicator Exposure Monitoring.  The advantages of CMA data over other surrogate data sets is that the chemicals and the job functions of mixer/loader/applicator were defined based on common application methods used for antimicrobial pesticides.  A few of the deficiencies in the CMA data are noted below:

- The inhalation concentrations were typically below the detection limits, so the unit exposures for the inhalation exposure route could not be accurately calculated.

- QA/QC problems including lack of either/or field fortification, laboratory recoveries, and storage stability information.

- Data have an insufficient amount of replicates.

The Pesticide Handlers Exposure Database (PHED):

The Pesticide Handlers Exposure Database (PHED) has been developed by a Task Force consisting of representatives from Health Canada, the U.S. Environmental Protection Agency (EPA), and the American Crop Protection Association (ACPA).  PHED provides generic pesticide worker (i.e., mixer/loader and applicator) exposure estimates.  The dermal and inhalation exposure estimates generated by PHED are based on actual field monitoring data, which are reported generically (i.e., chemical specific names not reported) in PHED.  It has been the Agency’ policy to use surrogate or generic exposure data for pesticide applicators in certain circumstances because it is believed that the physical parameters (e.g., packaging type) or application technique (e.g., aerosol can), not the chemical properties of the pesticide, attribute to exposure levels. [Note: Vapor pressures for the chemicals in PHED are in the range of E-5 to E-7 mm Hg.]  Chemical specific properties are accounted for by correcting the exposure data for study specific field and laboratory recovery values as specified by the PHED grading criteria.

PHED handler exposure data are generally provided on a normalized basis for use in exposure assessments.  The most common method for normalizing exposure is by pounds of active ingredient (ai) handled per replicate (i.e., exposure in mg per replicate is divided by the amount of ai handled in that particular replicate).  These unit exposures are expressed as mg/lb ai handled.  This normalization method presumes that dermal and inhalation exposures are linear based on the amount of active ingredient handled.