GM is petitioning the agency for inconsequentiality concerning 1,074 MY 2006 Cadillac XLR vehicles for failing to conform to the requirements of Federal Motor Vehicle Safety Standard No. 108, “Lamps, Reflective Devices, And Associated Equipment."  Some vehicles have a left hand and/or right hand headlamp assembly with a horizontal aiming adjuster that was not disabled by the supplier prior to being shipped to the vehicle assembly plant.  06V-041