CASTNET IV Statement of Work (SOW)

Project Background

The Clean Air Status and Trends Network (CASTNET) is a long-term environmental monitoring network that measures changes in ambient air quality and assesses atmospheric deposition over broad geographic regions of the U.S.  Operating since 1987, CASTNET has evolved into a robust regional monitoring program which currently consists of 84 monitoring stations nationwide.  The Environmental Protection Agency (EPA) operates a majority of the CASTNET monitoring stations.  In cooperation with the EPA, the National Park Service (NPS) currently operates 25 stations.  Table 1 and Figure 1 list and provide the location of the EPA operated CASTNET sites as of October 2007.  The primary monitoring objectives of CASTNET are to:

- Provide atmospheric data on atmospheric deposition, rural ground level ozone and other forms of atmospheric pollution;

- Monitor the status and trends in regional air quality and atmospheric deposition;

- Assess and report on geographic patterns and long-term, temporal trends in ambient air pollution and atmospheric deposition;

- Improve our understanding of PM and ozone formation;

- Validate and improve atmospheric models;

- Provide data for health-based research and epidemiology studies;

- Assess the effectiveness of EPA’s emission reduction programs and

- Support science and ecosystem studies.

Each CASTNET dry deposition site measures weekly average concentrations of sulfate (SO42-), nitrate (NO3-), ammonium (NH4+), sulfur dioxide (SO2), nitric acid (HNO3), chloride (Cl-) and the base cations (Na+, K+, Mg2+& Ca2+) using a 3-stage filterpack.  In addition, each site measures hourly meteorological conditions required for calculating dry deposition rates, most sites measure average hourly ambient ozone levels and select sites measure hourly trace-level reactive odd nitrogen (NOy), nitric oxide (NO), sulfur dioxide (SO2) and carbon monoxide (CO).  Table 2 is a list of pollutant monitoring and meteorological measurement systems deployed at a typical EPA CASTNET dry deposition site.

Dry deposition is calculated in the Network as a product of measured ambient air concentration values and inferentially-derived deposition velocities.  Historically, the Multi-layer Model (MLM) has been used to estimate deposition velocities, accounting for stomatal and boundary layer resistance to deposition at multiple levels in a canopy.  A new, more accurate model, the Multi-layer Biogeochemical Model (MLBC) is currently under development by EPA.  This model is built on the MLM but also accounts for plant photosynthesis and respiration in estimating deposition velocities.

CASTNET, a long-term regional monitoring program, is critical for characterizing trends in deposition levels and identifying relationships among emissions, atmospheric loadings, ecological effects and human health.  The EPA under several different mandates as well as other government agencies and the scientific community rely on the data and information from CASTNET, used in conjunction with information from other national monitoring networks (e.g., the National Atmospheric Deposition Program/National Trends Network (NADP/NTN) and Interagency Monitoring of Protected Visual Environments (IMPROVE)), to evaluate the effectiveness of air pollution control strategies for regional areas and assess chemical changes in the atmosphere.  CASTNET tracks real-world environmental results over time and space as emission reductions take place.  Since atmospheric changes occur very slowly and trends are often obscured by the wide variability of measurements and climate, numerous years of continuous and consistent data are required to overcome this variability.

The EPA’s Office of Atmospheric Programs administers CASTNET and is committed to regional atmospheric monitoring to assess long-term environmental trends.  The Clean Air Markets Division (CAMD), Office of Atmospheric Programs (OAP), is the lead in providing support and technical direction for CASTNET.  Additional background information, current standard operating procedures (SOPs), and the CASTNET Quality Assurance Project Plan (QAPP) are available at http://www.epa.gov/castnet.

SOW Organization

The Offeror shall provide the necessary technical support as described in this SOW to assist the EPA in operation of the CASTNET program.  The scope of this SOW includes specific requirements for the Core operation of the CASTNET program (Task 1) with additional tasks following to account for the number of EPA-sponsored CASTNET sites. The monetary value, technical time and operational needs vary with the number of EPA-sponsored sites and are reflected in these additional tasks.

Task 1, Core operations of the CASTNET Program includes requirements such as database management, quality assurance, training, data acquisition, field calibrations, reporting and participation in scientific meetings/conferences.  Task 1 includes all procedures that are independent of or only partially dependent on the number of monitoring sites or execution of additional tasks.

Some, but not necessarily all, additional tasks will be performed at each site to allow flexibility in operation of the network.  Additional tasks shall be funded incrementally.  For example, the Offeror shall propose a cost for the operation of one dry deposition filterpack at an average site.  The final compensation amount will be the product of the price of operating one dry deposition filterpack multiplied by the number sites which a dry deposition filterpack was operated.

Many of the activities associated with the additional tasks are dependent on whether the Offeror will be required to provide an operator at the site to perform the duties or if a local collaborator will perform the on-site duties for the task.  For example, in operating a dry deposition filterpack at the CASTNET site in Beltsville Maryland (BEL116) the Offeror would provide all services for the operation of the site; at the Cherokee Nation site (CHE185) the Cherokee Nation provides an operator for the routine tasks, but the Offeror would perform the semi-annual instrument calibration checks and other non-routine duties.

For the purposes of this solicitation, the Offeror shall assume operation of the 59 EPA-sponsored sites and manage data and coordinate network activities for 25 NPS-sponsored sites.  The Offeror shall provide a proposal for the Core operations of the CASTNET Program (Task 1) with the additional Required Tasks proposed and priced individually.  In preparing cost estimates for the additional tasks, the Offeror shall compensate for any incremental costs to the Core program (Task 1) incurred by adding the additional task at one site.

The EPA anticipates services described in this section to initiate upon award of the contract.  During a 90-day transition period beginning no later than 15-days after the contract award date the Offeror shall begin coordinating the transition of operation of the network with the existing CASTNET contractor and shall begin operating all aspects of the network at the end of the 90-day transition period.  Transition activities shall include the extraction and analysis of up to 100 filter or filtrate samples provided by EPA to establish comparability of the Offeror’s laboratory analyses with historical analyses.

Required Tasks

Task 1:  Core Operations of the CASTNET Program

The following sections describe the specific requirements for the Task 1 or the Core operations of the Network.  In addition to these specific requirements, the Offeror shall implement the transition plan as outlined in their technical proposal.  Management and costs of the site utilities, telemetry (e.g., phone or internet service) and the site land lease shall be included as a Level of Effort task and shall not be included in costs of this task.

1.1	Data Management and Analysis

The Offeror shall be responsible for storage and reporting of all information described in this Statement of Work, and shall maintain an archive of historical operations, deposition and air quality data acquired during previous contract periods.

The Offeror shall be responsible for acquiring, installing and running the MLM and/or MLBC, as specified in technical direction by the Contract Officer Representative (COR), using appropriate model inputs.  The EPA shall supply the Offeror with the most recent compiled modeling programs.  The Offeror shall be responsible for producing and maintaining input files required by the model programs and for loading model output files into the database through documented scripts and procedures.  All software, scripts and documentation developed under this contract shall be available to the EPA and delivered upon request.

1.1.1	Data Management & Storage

To manage and report this information efficiently and accurately while continuing to acquire data from on-going operations, the Offeror shall manage a relational database in a development/testing/production environment.  The database management system (DBMS) that the Offeror uses shall be capable of:

	Providing data security in compliance with the EPA requirements for external data systems;

	Efficiently managing a database of approximately 30 gigabytes in size;

	Efficiently managing a database having over 100 tables, with some tables having approximately 100 million records and

	Providing system-level user access and data integrity constraints.

The EPA currently uses the Oracle® Enterprise Database 10g Release 2(10.2.0.1.0) DBMS in a Solaris 10 environment.  The EPA anticipates that this platform will be used throughout the life of this contract, although upgrades to the DBMS and operating system are likely.  A description of the CASTNET schema is included in Attachment 1.  Upon award of the contract the EPA shall deliver to the Offeror a complete and functional archive of the current contractor's Microsoft SQLServer database and Visual Basic data management application, and a complete and functional export of the EPA's Oracle schema.

The Offeror shall be responsible for managing all information described in this Statement of Work, including the data management activities required for data collection, processing, validation, storage, documentation and reporting.  The types of data include, but are not limited to:

	All continuous measurements, observations and equipment status monitoring generated by the Network.  All continuous data and equipment status monitoring shall be stored in the database as hourly averages.  All observations made by the field operators shall be acquired either electronically (e.g., email or Web site) or through data transcription from hard copy forms sent in by the site operator.

	Results of laboratory analyses, including those types for routine samples, routine quality assurance samples, samples for method development or special studies, internal and external laboratory audits, internal and external system audits, and inter-laboratory comparisons.  All laboratory results shall include identification in the database by type of sample.

	Site status and location data: including latitude, longitude, elevation, FIPS codes, nearby NADP sites, political address (e.g., country, state, and county), conditions and surroundings within 1 km, history of instrumentation of the site, site contacts, and site operators and their contact information.

	Site photos and maps.  All site photos shall be stored as binary objects in the database or as references to electronic images.  The referenced electronic image shall be considered part of the database.

	Measurements and criteria from field calibrations and audits.

	Model results.

	Inter-network comparisons and other special studies.  All sampling and analysis data from inter-network comparisons and other special studies shall be identified, documented and stored in the database.

	Quality assurance information from routine and non-routine sources.  Data from routine and non-routine quality assurance measurements shall be identified, documented and stored in the database.

	The National Park Service’s (NPS’s) CASTNET data.  The Offeror shall import and manage all available data acquired by the NPS for the operation of their CASTNET sites for all types of data listed above.  The NPS or their designee will deliver data electronically to the Offeror in a format agreeable to all parties.

	External data sources.  The Offeror shall be responsible for acquiring and managing final data products from NADP/NTN wet deposition database, and IMPROVE aerosol data.  These external data products shall be used for estimating total (wet + dry) deposition and network-intercomparisons, respectively.

The Offeror shall maintain a data dictionary of all objects within the database, including tables, columns, constraints, and data validation codes.  The Offeror shall use established good data practices to ensure that database objects and applications developed by the Offeror have been properly tested and documented before use in the production environment.  The Offeror shall ensure that all electronic data acquisitions and transfers into and from the database are accurate and complete by checksum comparisons, or equivalent methods.

1.1.2	Data Reporting

The Offeror shall deliver data to the EPA for loading into the EPA database with a minimum amount of human intervention.  The Offeror shall transfer data to the EPA with an electronic agent (e.g., Oracle® Corporation’s SQL*Net™), or by creating and delivering electronic data on a routine basis that are compatible with the EPA’s DBMS.  If the Offeror requires connection to the EPA servers for data transfers, the Offeror must conform to requirements for access to the EPA servers described at http://yosemite.epa.gov/OEI/webguide.nsf/started/getserv , and shall have sufficient Internet bandwidth to efficiently transfer data.

All data collected utilizing 40 CFR Part 58 requirements shall be submitted to the AQS database utilizing AQS protocol.  AQS manuals and guides may be reviewed at http://www.epa.gov/ttn/airs/airsaqs/manuals/manuals.htm.  All ozone data and continuous PM2.5 mass data shall be automatically polled and uploaded to the AirNow webpage within 1-hour after a data collection hour is complete.

All data acquired through this contract shall be available to the EPA on a routine schedule, or in response to ad hoc data requests from the COR.  The EPA Project Officer shall determine the timing and content of deliveries pursuant to the contract Technical Direction Clause.  An electronic replica of the database and all supporting applications shall be delivered to the EPA annually.  Data deliveries shall include but not be limited to validated primary measurements from continuous monitors, sampling information, analytical results, laboratory quality assurance data, inter-laboratory comparisons, model results, time aggregations, data from special studies, and documentation for all database objects.  Documentation of all database objects shall be included within the database, and shall be clear and succinct with a minimum of jargon.  Preference will be given to those offers that are able to deliver or make available to the EPA screened continuous field data within 24-hours of data acquisition, either through secured Web query forms or uploading to the EPA servers.

1.1.3	Data Archiving

The Offeror shall maintain historical archives of CASTNET data from its inception, including primary measurements from continuous monitors, sampling information, analytical results, laboratory quality assurance data, inter-laboratory comparisons, model results, site locations and configurations, data from special studies, and data from other organizations used in the CASTNET program.

1.1.4	Data Security and Disaster Recovery

The Offeror shall provide for data security and deliver a detailed disaster recovery plan to the COR within 90-days of contract award.  The disaster recovery plan shall include all elements of good data management practices, including an effective backup strategy; off-site storage of database backup files, critical software and electronic documents; and an effective data restoration plan that provides for a minimum of data loss in the event of a disaster.

1.1.5 	Data Analysis

The Offeror shall be capable of performing complex statistical analyses (e.g., principal component, cluster and time series analyses) using a robust statistical analysis package (e.g., SAS, S-plus, and R).

The Offeror shall be capable of performing basic geographic and geostatistical analyses such as calculating geographic means and creating interpolations of geographic data sets using Inverse Distance Weighted, Kriging and Co-Variant Kriging algorithms; and producing publication-quality maps from these analyses.

1.1.6	Data validation

The Offeror shall screen and validate data from continuous field measurements for reasonableness using historical criteria, physical constraints, equipment status or other established and documented criteria.  All data shall be screened for data anomalies by applying screening checks for physical maximum, minimum, reasonable boundaries, rate of change, allowable characters or other documented criteria.  Any changes to raw data shall be recorded in the database and identified with a data validity code that identifies the circumstance or criteria by which the determination was made that the data is anomalous.  All data entered by human data entry shall be validated either by independent double entry or statistically defensible means to document a minimum of 99.99 percent data accuracy.  The Offeror shall screen, validate, code and submit all data collected in compliance with 40 CFR Part 58 to the EPA Air Quality System (AQS) database.

1.1.7	Model operation

The Offeror shall be responsible for acquiring, installing and running the MLM and/or MLBC, as specified in technical direction by the COR, using appropriate model inputs.  The EPA shall supply the Offeror with source code and executables compiled under MS-Windows for the most recent modeling programs.  The Offeror shall be responsible for producing and maintaining input files required by the model programs and for loading model output files into the database through documented scripts and procedures.  All software, scripts and documentation developed under this contract shall be available to EPA and delivered upon request.

1.2	Quality Assurance

The Offeror shall prepare and deliver a Quality Management Plan (QMP) as part of the proposal.

Quality Assurance (QA) includes, but is not limited to, those activities conducted by and for the Offeror’s management that assure and evaluate the effectiveness and appropriateness of all monitoring-related processes that might affect the quality of data delivered to the EPA under the contract.  Typically, QA activities shall ensure that the Quality Control (QC) functions are carried out as designed into the operational functions of the work.  The Offeror shall periodically evaluate the timeliness, effectiveness, and appropriateness of the QC activities, as outlined and specified in the QA guidance.

The Quality Management Plan (QMP) and Quality Assurance Project Plan (QAPP) are critical planning documents for any environmental data operation.  The corporate QMP defines an organization’s QA-related policies, criteria for and areas of application, and definition of roles, responsibilities, and authorities.

The QAPP documents how environmental data operations are planned, implemented, and assessed during the life cycle of program, project, or task.  The purpose of the QAPP is to define in detail how specific QA and QC activities will be implemented during this project.  Standard Operating Procedures (SOPs) document in detail the routine or repetitive administrative and technical activities to facilitate consistency and integrity of the product.  SOPs facilitate activities that are managed under a QAPP.

The Offeror shall prepare a draft comprehensive QAPP, including all related manuals and SOPs, and deliver four printed copies to the EPA for comments within 90-days of contract award.  After receipt of the EPA comments, the Offeror shall deliver within 30-days one copy of the plan to the EPA QA Officer for approval.  Upon approval by the EPA QA Officer, the Offeror shall deliver four printed copies and an electronic version of the plan to the EPA.

The QAPP and all associated documents shall conform to EPA general guidance and guidance for non-EPA organizations, as described at http://www.epa.gov/quality/qa_docs.html.  The QAPP will include all of the elements describe in the “EPA Requirements for QA Project Plans”, EPA QA/R-5 (EPA/240/B-01/003).  The QAPP and SOPs shall be based, as applicable, on the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, II, and IV.  At a minimum, these documents shall provide sufficient detail of all aspects of the CASTNET operation to allow a user to perform the same activities and measurements and achieve similar results, and shall include the operational aspects of all sites within the CASTNET program regardless of operating agency.  Method summaries and SOPs will be provided by the EPA for those equipment and procedures operated or performed by other agencies which differ from those of the Offeror.

The QA/QC program shall provide a uniform basis for sample handling, analysis, instrument and/or methods calibration and maintenance, equipment and method acceptance testing, performance evaluation, analytical data gathering, data processing and analysis, and reporting.  In many instances where methodologies are available, specific QC procedures are incorporated into the method documentation.

The Offeror shall perform quality assurance activities independent of project management. The Offeror’s quality assurance team shall prepare and deliver to the EPA four quarterly reports within 30-days of the end of the calendar quarter for each option year of the contract.  The quarterly reports will briefly describe and summarize systematic data quality issues identified and remedial actions taken during the quarter.  Systematic data quality issues are defined as procedures or equipment within the project that may be introducing unacceptable bias or uncertainty into the data.  The Offeror’s quality assurance team shall also prepare and deliver to the EPA an annual report summarizing the current quality state of the CASTNET program, as measured by the various quality control indicators.

1.3 Equipment Depot/Equipment Repair and Maintenance

The Offeror shall purchase new equipment and parts for the on-going operation and enhancement of the network on behalf of the EPA.  Equipment and parts shall be delivered to the Offeror’s facility or installation sites.  Prior to deploying equipment for service, the Offeror shall ensure that field equipment is operating properly by performing and documenting acceptance testing of all the equipment purchased by EPA delivered to the Offeror’s facility.  Acceptance tests shall include comparisons of instrument outputs to known, calibrated values and checks of zero, span, and drift, noise levels, response time, and detection limits.  The Offeror shall notify the EPA COR and should return to the manufacturer any equipment that fails acceptance testing.

The Offeror shall ensure sufficient spare parts are on hand to meet or exceed the requirements of this contract and shall purchase spare parts on a periodic basis to ensure sufficient spare parts are available at all times.  The Offeror shall be responsible for affixing property tags properly to all EPA-purchased equipment and parts.

The Offeror shall maintain and update a database inventory of all EPA capital equipment.  The current equipment inventory is included in Attachment 2.  At a minimum, the inventory database shall contain the following fields: equipment description, manufacturer name, model number, serial number, EPA property number, location, purchase price, month and year of purchase, current condition and disposition.  For quality assurance purposes, the history of all ozone analyzers shall be traceable using this database.  The Offeror shall provide a written report on equipment inventory to EPA annually, and upon request by the PO.

The Offeror shall be responsible for the maintenance and repair (including costs) of all instruments, shelters, and data acquisition systems.  Routine maintenance and repair expenses shall be included in the relevant task pricing.  The Offeror shall insure that all equipment is in good working condition, is conducive to a safe work environment and there is appropriate protection of the Network equipment.  The equipment shall be Government Furnished Property (GFP) or Offeror Acquired Property (CAP).  The EPA may require equipment to be upgraded as new techniques, instrumentation, and improved components become available, and may require the replacement of outdated equipment that has reached the end of its operating lifetime.  New or replacement equipment shall be government furnished equipment.

1.4 	Data Acquisition System

The Offeror shall use an automated data acquisition system.

1.5 	Training (site operators)

The Offeror shall provide standard substantive, hands on training to each new site operator. Training topics shall include, but not be limited to, an overview of the CASTNET program, equipment operation and maintenance, sampling procedures, safety, documentation and quality assurance.  Particular emphasis shall be placed on training operators on instrument installation, equipment calibrations, maintenance, repairs, and sample change-out procedures.  The Offeror shall evaluate operator performance in these activities, and provide adequate training until the site operator is proficient, in accordance with the data quality objectives.

1.6	Field Calibrations

The Offeror shall visit each active CASTNET monitoring station at least twice per year to perform routine calibration and maintenance of all CASTNET field equipment.  In preparing for site visits, the Offeror shall coordinate with site operators and notify the COR of all scheduled site visits no less than 2 weeks prior to monitoring site trips.  Upon arrival at each monitoring site and before any adjustments are made to any instruments, the Offeror shall conduct and record complete performance checks on all air quality systems, meteorological instruments, and data acquisition systems.

The Offeror shall perform the field calibrations listed in Table 3 at each site using the specified method, or an equivalent or better method that meets the acceptance criteria listed in Table 3.  The Offeror shall operate all data collection activities in accordance with the quality assurance documentation described in section 1.2 of this SOW.

1.7	Meetings and conferences

The EPA COR may request the Offeror to attend and participate in conferences or meetings related to atmospheric deposition, air pollution or the operation of CASTNET.  For the purposes of this solicitation, the Offeror should assume 10 travel days annually for these requests.

1.8	Reporting

The Offeror shall deliver to the EPA a monthly progress report summarizing the network operation and maintenance activity for the prior month.  At a minimum, the monthly progress report shall describe: any significant events or changes to the network that would affect interpretations of results; site activity; quality assurance procedures; data management; monthly billing (in excel format); and any issues or limitations in using the data.

The Offeror shall deliver to the EPA an annual report summarizing the network for the prior calendar year.  At a minimum, the annual report shall describe: the status of the network; any significant events or changes to the network that would affect interpretations of results; results and significant findings of the network; the quality of data produced by the program; any issues or limitations in using the data.

1.9	Third Party Audits

The Offeror shall provide State and local agencies with access to CASTNET sites for the purpose of audits, installation of data loggers or installation and operation of additional monitoring equipment as space permits.  For the purpose of costing, no more than 10 sites will be visited by State or local agencies per year.

The Offeror shall provide third party auditors access to CASTNET sites as well as the Offeror’s facility for the purpose of quality assurance audits and technical system audits.  For the purpose of this solicitation the Offeror shall assume third party auditors will visit each monitoring site and the Offeror’s facility once per year.

Task 2:  Dry Deposition Filterpack

Particles and selected gases shall be collected by passing air at controlled flow rates through a sequence of Teflon®, nylon, and base-impregnated filters.  The Offeror shall perform filter pack sampling 10-meters above ground surface using a tilt-down tower.  Filter pack flow shall be maintained with mass flow controllers at standard conditions of 25°C and 101.33 k Pascal (760 mmHg).  Flow shall be maintained at 1.5 liters per minute (LPM) at sites having higher concentrations of analytes (generally sites in the Eastern U.S.) and 3.0 LPM at sites having lower concentrations (generally sites in the Western U.S.) or at other flow rates upon technical direction from the COR.  Filter packs shall be replaced at each site every Tuesday at approximately 0900 hours by a site operator employed directly by the Offeror or as a subcontractor.  SOPs and the CASTNET QAPP describing filterpack operations are available at http://www.epa.gov/castnet.

Task 3	:  Ozone Monitoring (current CASTNET operating protocol)

The Offeror shall operate ozone analyzers in accordance with the CASTNET QAPP and SOPs available at http://www.epa.gov/castnet.  Inlets for the ozone analyzers shall be mounted at 10-meters above ground using a tilt-down tower.  The CASTNET stations utilize a Thermo Electron Corporation Model 49-103/49C/49i-with onboard ozone generator/transfer standard.  The ozone analyzers shall be automatically challenged daily with a calibration atmosphere of 0 ppm, and 0.400 ppm and 0.090 ppm (zero, span and precision check or Z/S/P).  Ozone analyzers multi-point calibration checks shall be performed at least 1/6-months.  The onboard ozone (generator) transfer standard shall be challenged with an EPA Quality Assurance Handbook compliant ozone transfer standard at least 1/6-months.

Task 4:  Ozone (40 CFR Part 58 compliant)

The offeror shall operate an ozone analyzer in accordance with 40 CFR Part 58; the guidance in “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II; “Technical Assistance Document Transfer Standards for Calibration of Air Monitoring Analyzers for Ozone” (EPA-600/4-79-056); and “Technical Assistance Document for the Calibration of Ambient Ozone Monitors” (EPA-600/4-79-057).

The onboard ozone generator will be utilized as the station ozone transfer standard.

The Offeror shall be responsible for submitting data to the AQS database.

Task 5:  Meteorology

Wind speed, wind direction, relative humidity, solar radiation, precipitation, surface wetness, temperature and delta temperature measurements shall be made in accordance with the “Quality Assurance Handbook for Air Pollution Measurement Systems”

Volume IV: Meteorological Measurements (EPA-454/D-06-001).

Task 6:  Trace gas NOy

The Offeror shall operate a NOy/NO analyzer according to the manufactures manual and recommendation, the operation shall be consistent with 40 CFR Part 58, the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II and the “Technical Assistance Document (TAD) for Precursor Gas Measurements in the NCore Multi-pollutant Monitoring Network” (EPA-454/R-05-003) available at http://www.epa.gov/ttn/amtic/pretecdoc.html.  The Offeror shall be responsible for submitting data to the AQS database.

Task 7:  Trace gas SO2

The Offeror shall operate a trace gas SO2 analyzer according to the manufactures manual and recommendation, the operation shall be consistent with 40 CFR Part 58, the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II and the “Technical Assistance Document (TAD) for Precursor Gas Measurements in the NCore Multi-pollutant Monitoring Network” (EPA-454/R-05-003) available at http://www.epa.gov/ttn/amtic/pretecdoc.html.  The Offeror shall be responsible for submitting data to the AQS database.

Task 8:  Trace gas CO

The Offeror shall operate a trace gas CO analyzer according to the manufactures manual and recommendation, the operation shall be consistent with 40 CFR Part 58, the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II and the “Technical Assistance Document (TAD) for Precursor Gas Measurements in the NCore Multi-pollutant Monitoring Network” (EPA-454/R-05-003) available at http://www.epa.gov/ttn/amtic/pretecdoc.html.  The Offeror shall be responsible for submitting data to the AQS database.

Task 9:  PM2.5 FRM mass

The Offeror shall operate a PM2.5 FRM mass sampler 24 hr. average every 3rd day according to the manufactures manual and recommendation.  The operation shall be consistent with 40 CFR Part 58 and the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II.  The Offeror shall be responsible for submitting data to the AQS database.

Task 10:  PM2.5 speciation of organic and elemental carbon, major ions and trace metals

The Offeror shall operate a PM2.5 speciation sampler 24 hr. average every 3rd day according to the manufactures manual and recommendation.  The operation shall be consistent with the Speciation Trends Network (STN) protocol, 40 CFR Part 58, the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II and in accordance with quality assurance documentation at http://www.epa.gov/ttn/amtic/specqual.html.  The Offeror shall be responsible for submitting data to the AQS database.

Task 11:  PM10-2.5 FRM mass

The Offeror shall operate a PM10-2.5 FRM mass sampler 24 hr. average every 3rd day according to the manufactures manual and recommendation.  The operation shall be consistent with 40 CFR 58 and the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II.  The Offeror shall be responsible for submitting data to the AQS database.

Task 12:  PM10-2.5 speciation of organic and elemental carbon, major ions and trace metals

The Offeror shall operate a PM10-2.5 speciation sampler 24 hr. average every 3rd day according to the manufactures manual and recommendation.  The operation shall be consistent with 40 CFR Part 58 and the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II.  The Offeror shall be responsible for submitting data to the AQS database.

Task 13:  Continuous PM2.5 mass

The Offeror shall operate a continuous PM2.5 mass sampler 1 hour reporting interval – utilizing Beta Attenuation Monitoring (BAM) according to the manufactures manual and recommendation.  The operation shall be consistent with 40 CFR Part 58 and the “Quality Assurance Handbook for Air Pollution Measurement Systems”, Volumes I, and II.  The Offeror shall be responsible for submitting data to the AQS database.

Task 14:  Filterpack preparation and laboratory analysis

The Offeror shall be responsible for providing sample preparation and analytical services for two types of samples: 1) sample filters, and 2) precipitation samples for inter-laboratory comparisons.  The Offeror shall maintain the technical capability to perform the required analytical services and provide an acceptable level of personnel, equipment, and systems.  The Offeror’s responsibilities shall include, but not be limited to, the following:

	Purchase, maintenance, and pre-sampling treatment of all required filter media;

	Appropriate shipping containers and shipment of all filter media to the field, including field blanks;

	Analysis of all samples, laboratory quality control samples, blanks, calibration standards, filter production-lot acceptance testing and performance evaluation samples;

	All sampling and analysis data entry;

	Purchase and maintenance of laboratory instruments and consumable supplies; and

	Storage and archival of all sample extracts and filter media.

For the purposes of this bid, Table 4 lists the maximum and minimum numbers of samples that will be submitted for the base year and each of the four option years.

14.1	Interlaboratory Comparison Samples

The Offeror shall analyze precipitation and natural water laboratory inter-comparison samples for anions (SO42- and NO3-), base cations (Na+, Ca2+, K+, and Mg2+), ammonium (NH4+), and pH using the methods specified in Table 5.  Each sample shall be analyzed for the complete set of analytes.  Inter-laboratory comparison studies are necessary for the documentation of laboratory performance and coordination of results with other North American monitoring networks, including IMPROVE, the Canadian Acid Precipitation Monitoring Network (CAPMoN), and NADP.

14.2	Filter Pack Samples

The Offeror shall analyze filter media for anions (SO42- and NO3-), base cations (Na+, Ca2+, K+, and Mg2+) and ammonium (NH4+).  Each sample shall be analyzed for the complete set of analytes.  The Offeror shall prepare the media and filter packs for deployment into the field, ship the filter packs to each site, receive and log the filter packs after sampling, disassemble the filter packs, extract the filters, analyze the extracts, and report results.

14.2.1	Filter Pack Preparation and Media Acceptance Testing

The Offeror shall be responsible for the purchase and preparation of all filter media.  Each three-stage filter pack shall contain a Teflon® filter, a nylon filter, and two base-impregnated cellulose Whatman® filters.  The Offeror shall be responsible for impregnating the cellulose filter with potassium carbonate.  Upon direction by the PO, the Offeror shall coordinate the purchase of filter media with other monitoring networks to ensure consistency in sample results.

The Offeror shall perform acceptance tests on all filters before assembly.  Acceptance testing shall include the extraction and analysis of a sufficient number of filters from each type of filter box to determine with 95 percent confidence that analyte contamination for the box of filters does not exceed 2 times the method detection limit.  Prior to loading of filters, each three-stage filter pack assembly shall be cleaned with deionized water, oven-dried, assembled and inspected for damage.

The Offeror shall ship filter packs to field sites for sampling.  Filters shall not be used more than 30 days after preparation.  Laboratory blank samples shall be prepared as the filter packs are prepared.  In addition, filter blank samples shall be sent to the field quarterly in order to evaluate the effects of preparation and shipping on sample media.

14.2.2	Filter Extraction

After sampling in the field, filter packs shall be shipped from the field sites and disassembled for extraction and analysis.  The Offeror shall extract all filters using methods that produce extraction efficiencies comparable to historical CASTNET filter extraction methods.  Sample extracts shall be stored at 4 degrees Celsius for at least 8 hours prior to analysis.

14.2.3	Analysis of Filter Extracts

The Offeror shall analyze filter extracts using the methods specified in Table 6 or an equivalent or better method which has been approved by the EPA.

14.3	Sample Handling, Custody, and Storage

After field sampling is completed, samples shall be sent back to the laboratory where they shall be received, labeled, and inspected for damage.  Samples shall be stored at 4C before and after analysis.  Extracts shall be stored for a minimum of two years after the collection of the sample.  Samples shall be tracked and managed using an automated tracking system such as bar codes or optical character recognition.

14.4	Data Acquisition and Management

The Offeror shall use a laboratory information management system (LIMS) for automatic data acquisition, efficient sample tracking and laboratory data management to the fullest extent practicable.  The Offeror shall use an automated data acquisition system or provide for and document a minimum 99.99 percent data accuracy of manually entered data for all laboratory data acquisition.  All data entered by manual data entry shall be validated either by independent double entry or statistically defensible means to document the minimum data accuracy.

14.5	Laboratory Quality Assurance

In order to maintain an acceptable quality of data and to establish estimates of accuracy and precision, the Offeror shall have quality assurance procedures for laboratory analysis in place. The Offeror shall randomly replicate 5% of the samples within an analysis to assess precision.

The Offeror shall analyze the following quality control standards:

	A NIST-traceable Calibration Verification Standard produced by an independent lab shall be run after every 10 environmental samples and at the end of the batch to track instrument drift;

	A NIST-traceable reference standard produced by an independent lab shall be analyzed at the beginning and end of each run to assess accuracy;

	One method blank shall be analyzed with each extraction and

	For Ion Chromatography analyses, internal injection standards shall be prepared to assess shifts in retention time and sample injection volume.

Calibration curves shall be generated for all analyses, and all samples must fall within range of the calibration curve.  Quality control standards, calibration curves, sample replicates, and filter blanks must meet the specified acceptance criteria (See Table 6).  The Offeror shall document in the Quality Assurance Project Plan corrective actions for samples that do not meet these acceptance criteria.  Quality assurance analyses shall be reported to the EPA quarterly using accepted laboratory methods for aggregating and calculating statistics.

To minimize the occurrence of instrument failure and system malfunctions, the Offeror shall be responsible for instrument calibration, inspection, testing, and maintenance including, but not limited to, lubrication of pumps, prevention of instrument leaks, and maintenance and replacement of valves and fittings.

Task 15:  Operation of NADP site

National Atmospheric Deposition Program (NADP) is structured as a cooperative program that represents coordinated efforts of many interested individuals and organizations to operate monitoring sites, report data, and oversee research activities related to atmospheric deposition.  For more information on NADP, visit: http://nadp.sws.uiuc.edu.

Each NADP site has a sponsoring agency and an operating agency.  For some sites the sponsoring and operating agencies may be the same.  Site sponsors and operating participants are responsible for ensuring that the equipment, facilities, materials, resources, and people are available to operate and maintain the site.  Uniformity is essential to obtain data on how the chemical climate in the nation’s ecological regions is changing over seasons, years, and even decades.  This helps ensure the data are geographically representative and comparable from site to site and are an essential part of any long-term environmental monitoring network.  Sites must conform to fixed site selection and installation criteria and follow standard procedures for collecting, handling, and measuring samples (NADP 2003).  The EPA currently sponsors and provides operational support for several NADP network sites as well as supports a quality assurance program.  The program provides information on the conditions of each site and helps determine if site equipment is functioning properly and samples collection and data provided by the site operators are in conformance with NADP standard operating procedures.

15.1	Purpose

The primary purpose of Task 15 is to provide for the costs of site operators responsible with maintaining EPA-sponsored NADP sites collocated with CASTNET sites (Table 7).

The site operator has primary responsibility for monitoring equipment operation and maintenance, physical maintenance of the site (e.g., maintaining NADP local siting criteria), weekly collection and measurement of samples, sample documentation, and submission of samples and documentation to the Central Analytical Laboratory (CAL).  One or more observers may assist the site operator in these responsibilities.  Excluding travel to the site, site operators generally spend about 2 hours performing the required weekly (every Tuesday) duties.  Through their diligence to these duties, site operators are largely responsible for determining the quality of NADP data.

Site Operator responsibilities include:

- Travel to the field site and inspect the site and equipment every Tuesday.

- Collect the wet side bucket from the collector and the Belfort gage chart every Tuesday.

- Install a new Belfort gage chart and clean collector bucket for the next sample every Tuesday.

- Perform routine equipment maintenance or repairs as needed or prescribed.

- Transport the bucket and Belfort gage chart to the field laboratory.

- Weigh the bucket and transfer the sample it contains to a sample bottle.

- For samples of 70 grams or more, remove a portion from the sample bottle to measure sample pH and conductivity.

- Read and interpret the event recorder and precipitation records on the Belfort gage chart to the CAL within 48 hours of sample collection.

- Perform occasional special maintenance or quality assurance tasks in cooperation with the CAL or other agencies.

- Contact the CAL with any questions about equipment or procedures.

- In addition, the NADP Program Office sponsors an annual Field Operations Training Course for new and existing site operators.

Occasional non-routine visits by the site operator, and the costs of shipping (sample and document transfer) shall be included in the total cost of maintaining these sites.

15.2 	Site Operation Support

The Offeror shall be responsible for providing the necessary site operator costs associated with maintaining six NADP sites as listed in Table 8.

The Offeror shall ensure that an available and trained site operator is performing the site operator duties as specified in the NADP Site Operation Manual (NADP 1999-01).  This also includes identifying a designated back-up site operator for each site in the event the primary site operator is not available.  In addition, shipping costs associated with sample and documentation transfer to the NADP Program Office will be considered for the EPA sponsored NADP sites both independent and collocated with CASTNET sites.  The Offeror shall allow for the possibility of one 2-day site visit if circumstances arise where travel to the site is necessary.  The Offeror shall allow for one or two trips to Champaign, IL for site operators to attend the annual NADP Field Operations Training Course.  NADP sites that are collocated with CASTNET sites are listed in Table 7.

15.3	NADP Siting Criteria Problems

The Offeror shall be responsible for resolving siting criteria issues, as practical, that are identified by the NADP Program Office’s Quality Assurance Manager or the Work Assignment COR.  For the purposes of estimating costs the Offeror shall assume 3 trips to EPA sponsored sites will be necessary for the year.  The Offeror shall work with the site operator to resolve the issues and notify the EPA Work Assignment COR when the issue(s) have been resolved.

Task 16:  Operation of IMPROVE site

The Interagency Monitoring of Protected Visual Environments (IMPROVE) program is a cooperative air quality monitoring effort governed by a steering committee composed of representatives from Federal Agencies: the Environmental Protection Agency, the National Oceanic and Atmospheric Administration, and the four federal land managers – the National Park Service, the U.S. Forest Service, the U.S. Fish and Wildlife Service, and the Bureau of Land Management.  In addition to the federal representatives the steering committee is comprised of regional organizations and state agencies and an associate member, the State of Arizona Department of Environmental Quality.  The IMPROVE monitoring program was established in 1985 to aid in the creation of federal and state implementation plans for the protection of visibility in Class I areas as stipulated by the 1977 Clean Air Act Amendments.  The monitoring network consists of (as of January 2006) 110 IMPROVE aerosol visibility sites and over 50 IMPROVE Protocol aerosol sampler sites, 15 transmissometers, 44 nephelometers, and 12 film and digital camera systems, 52 Web camera systems, among other monitoring activities.  Quality data collection begins with those who operate, service, and maintain monitoring instrumentation.  Therefore, it is important to have trained site operators to ensure that the monitoring station is functioning properly and IMPROVE standard operating procedures (SOPs) are followed.

CASTNET operated eight visibility or IMPROVE protocol sites through a contract to provide a core set of sites in the Eastern source regions.  The network support for these sites were transitioned to the IMPROVE program in 2001, however, EPA still provides support for site operations.  These IMPROVE sites are now referred to as EPA Protocol sites.  The IMPROVE program is anticipating a reduction in the number of sites due to decreases in supporting monitoring budgets.  The reductions will likely occur over time but may begin in FY08 and affect some of the eight sites associated with this work assignment.

The primary purpose of Task 16 is to provide for the costs of site operators associated with maintaining eight IMPROVE monitoring sites.  Eight sites currently receive funding for site operation by the EPA.  These include six sites that are collocated with CASTNET sites and two independent IMPROVE sites at Sikes, LA and Livonia, IN (Table 9).  In addition, occasional non-routine visits by the site operator, certain utilities, and the costs of land leases such as those for sites not collocated with CASTNET, shall be included in the total cost of maintaining these sites.  The site operator has primary responsibility for monitoring equipment operation and overall site maintenance (e.g., ensuring adherence with IMPROVE siting criteria), weekly collection and measurement of samples, sample documentation, and handling (submission of samples and documentation to the central laboratory).  One or more observers may assist the site operator in these responsibilities.  Excluding travel to the site, site operators generally spend about 2 hours performing their weekly duties under normal operating conditions.  Through their diligence to these duties, site operators are largely responsible for determining the quality of IMPROVE data.

The Offeror shall be responsible for providing the necessary site operator support and costs associated with maintaining eight IMPROVE monitoring stations (see Table 9).  This support may include other direct costs such as utilities (i.e., telephone or electric), land lease payments, occasional non-routine visits required by the site operator, and shipping costs associated with sample, equipment, or documentation transfers.  The Offeror shall ensure that an available and trained site operator is performing the site operator duties specified in the appropriate IMPROVE Site Operation Manuals.  This also includes identifying a designated back-up site operator for each site in the event the primary site operator is not available.  The Offeror shall also ensure the site operator calls the Offeror weekly on Tuesdays to report on site operation and sample collection.  The Offeror shall allow for the possibility of one or two site visits if circumstances arise where travel to the site is necessary.

Task 16:  Acquisition and Management of NPS data

The Offeror shall manage data and coordinate network activities for the CASTNET sites operated by the NPS.

Task 17: Level of Effort

In addition to the tasks described above, the Offeror shall provide:  extraneous infrastructure costs for sites; design, testing and deployment of new monitoring methods and technology for use at CASTNET sites; conduct non-routine monitoring activities; special studies or analyses associated with CASTNET or other assessments of emission control programs; as directed in task orders issued by the EPA Contracting Officer (CO).  Examples of these activities include:

- Management of the site utilities, telemetry (e.g., phone or internet service) and the site land leases;

- Operate or collaborate with (e.g., collect samples at, analyze samples for, or make CASTNET facilities available to) other integrated research monitoring programs, such as the NADP, IMPROVE or other monitoring networks approved by EPA;

- Deployment and operation of gaseous ammonia monitoring devices;

- Deployment and operation of denuder-filterpack monitoring devices;

- Deployment and operation of gaseous and particulate mercury monitoring equipment;

- Operate and maintain instruments for direct measurement of dry deposition or surface fluxes of ozone, sulfur dioxide, carbon dioxide, ammonia, nitric acid by relaxed eddy correlation or gradient methods;

- Assist in air quality or deposition model development and programming;

- Design and analysis of air quality databases and novel data acquisition systems;

- Acquire and submit air monitoring data to AQS;

- Select, evaluate and install equipment at candidate monitoring sites according to network requirements and criteria;

- Provide training and conduct workshops to State, Local, and Tribal personnel on air monitoring techniques and procedures;

- Install and operate soil monitoring equipment and institute procedures for critical loads assessments and validation;

- Prepare ad hoc summaries of data, associated data quality information, and statistical analyses of data for temporal or spatial trends.

Table 1. List of Active EPA CASTNET Monitoring Stations (October 2007)

| SITE_ID | SITE_NAME | STATE | LATITUDE | LONGITUDE |
| --- | --- | --- | --- | --- |
| ABT147 | Abington | CT | 41.8402 | -72.0100 |
| ALC188 | Alabama-Coushatta | TX | 30.4210 | -94.4045 |
| ALH157 | Alhambra | IL | 38.8690 | -89.6228 |
| ANA115 | Ann Arbor | MI | 42.4165 | -83.9020 |
| ARE128 | Arendtsville | PA | 39.9231 | -77.3078 |
| ASH135 | Ashland | ME | 46.6041 | -68.4135 |
| BEL116 | Beltsville | MD | 39.0284 | -76.8172 |
| BFT142 | Beaufort | NC | 34.8848 | -76.6203 |
| BVL130 | Bondville | IL | 40.0519 | -88.3724 |
| BWR139 | Blackwater NWR | MD | 38.4450 | -76.1114 |
| CAD150 | Caddo Valley | AR | 34.1795 | -93.0988 |
| CAT175 | Claryville | NY | 41.9422 | -74.5520 |
| CDR119 | Cedar Creek | WV | 38.8795 | -80.8477 |
| CDZ171 | Cadiz | KY | 36.7841 | -87.8499 |
| CHE185 | Cherokee Nation | OK | 35.7507 | -94.6700 |
| CKT136 | Crockett | KY | 37.9214 | -83.0662 |
| CND125 | Candor | NC | 35.2632 | -79.8365 |
| CNT169 | Centennial | WY | 41.3642 | -106.2399 |
| CON186 | Converse Station | CA | 34.1941 | -116.9130 |
| COW137 | Coweeta | NC | 35.0608 | -83.4306 |
| CTH110 | Connecticut Hill | NY | 42.4006 | -76.6538 |
| CVL151 | Coffeeville | MS | 34.0026 | -89.7990 |
| DCP114 | Deer Creek | OH | 39.6359 | -83.2605 |
| EGB181 | Egbert | ON | 44.2320 | -79.7812 |
| ESP127 | Edgar Evins | TN | 36.0388 | -85.7331 |
| GAS153 | Georgia Station | GA | 33.1787 | -84.4052 |
| GTH161 | Gothic | CO | 38.9564 | -106.9858 |
| HOW132 | Howland | ME | 45.2158 | -68.7082 |
| HOX148 | Hoxeyville | MI | 44.1809 | -85.7390 |
| HWF187 | Huntington Wildlife Forest | NY | 43.9731 | -74.2232 |
| IRL141 | Indian River Lagoon | FL | 27.8492 | -80.4554 |
| KEF112 | Kane Exp. Forest | PA | 41.5980 | -78.7674 |
| KNZ184 | Konza Prairie | KS | 39.1021 | -96.6096 |
| LRL117 | Laurel Hill | PA | 39.9878 | -79.2515 |
| LYK123 | Lykens | OH | 40.9173 | -82.9982 |
| MCK131 | Mackville | KY | 37.7046 | -85.0485 |
| MCK231 | Mackville Collocated | KY | 37.7046 | -85.0485 |
| MKG113 | M.K. Goddard | PA | 41.4271 | -80.1451 |
| OXF122 | Oxford | OH | 39.5327 | -84.7286 |
| PAL190 | Palo Duro | TX | 34.8803 | -101.6649 |
| PAR107 | Parsons | WV | 39.0905 | -79.6617 |
| PED108 | Prince Edward | VA | 37.1655 | -78.3069 |
| PND165 | Pinedale | WY | 42.9288 | -109.7880 |
| PNF126 | Cranberry | NC | 36.1058 | -82.0454 |
| PRK134 | Perkinstown | WI | 45.2066 | -90.5969 |
| PSU106 | Penn State | PA | 40.7208 | -77.9319 |
| QAK172 | Quaker City | OH | 39.9428 | -81.3373 |
| ROM206 | Rocky Mtn NP Collocated | CO | 40.2778 | -105.5453 |
| SAL133 | Salamonie Reservoir | IN | 40.8160 | -85.6611 |
| SAN189 | Santee Sioux | NE | 42.8292 | -97.8540 |
| SND152 | Sand Mountain | AL | 34.2888 | -85.9698 |
| SPD111 | Speedwell | TN | 36.4700 | -83.8268 |
| STK138 | Stockton | IL | 42.2869 | -89.9997 |
| SUM156 | Sumatra | FL | 30.1103 | -84.9903 |
| UVL124 | Unionville | MI | 43.6138 | -83.3591 |
| VIN140 | Vincennes | IN | 38.7408 | -87.4853 |
| VPI120 | Horton Station | VA | 37.3297 | -80.5578 |
| WSP144 | Wash. Crossing | NJ | 40.3125 | -74.8729 |
| WST109 | Woodstock | NH | 43.9450 | -71.7008 |

Figure 1. Map of Active EPA CASTNET Monitoring Stations (October 2007)

Table 2. List of pollutant monitoring and meteorological measurement systems deployed at a typical EPA CASTNET dry deposition site

| Field Equipment | Description | Application |
| --- | --- | --- |
| Ozone Analyzer | Thermo Electron Corporation Model 49-103/49C/49i-with onboard ozone generator/transfer standard | Measures continuous ambient O3 concentrations integrated over a hourly period |
| Wind Speed and Direction | Climatronics anemometer chopper wheel, Climatronics AIO weather station, R.M. Young Wind Monitor or F460 vane and translator, R.M. Young Wind Monitor | Input parameters to the Multi Layer Model |
| Temperature/Delta Temperature | Climatronics or R.M. Young temperature sensors | Input parameters to the Multi Layer Model |
| Relative Humidity | Climatronics model 100098 or Rotronics MP-100F humidity temperature probe | Input parameter to the Multi Layer Model |
| Solar Radiation | LI-COR pyranometer, silicon photovoltaic sensor with R.M. Young or Climatronics translator | Input parameter to the Multi Layer Model |
| Surface Wetness | R.M. Young wetness sensor | Input parameter to the Multi Layer Model |
| Precipitation | Climatronics 8-inch heated tipping bucket rain gauge | Input parameter to the Multi Layer Model |
| 3 Stage Filter Pack | Sequence of Filters: Teflon®, nylon, and potassium carbonate- impregnated Whatman® | Collects ambient concentrations of particulate SO42-, NO3-, NH4+, and gaseous SO2 and HNO3 integrated over weekly periods |
| Flow Control | Teledyne Hastings or Tylan Mass Flow Controllers | Maintains constant sample flow |
| Data Acquisition | Odessa DSM-3260 and DSM 3260L (backup) or Campbell Scientific CR3000 or ESC Model 8816 | Records data for select continuous measurement parameters |

Table 3. Field Calibration Acceptance Criteria

| Measurement | Method | Acceptance Criteria |
| --- | --- | --- |
| Filter Pack Flow | Mass Flow Controller | ± 2% of actual flow |
| Ozone UV absorbance1 Onboard Ozone Generator (Transfer standard) Local primary standard | ± 15% span ± 10 ppb zero; 1/2-days level one2 |
|  | Linearity error < 5%; Multipoint calibration 0 and 4 upscale points2 |
|  | ±4% or ±4 ppb (whichever greater) RSD of six slopes # 3.7% Std. dev. of six intercepts #1.5% New slope = ±0.05 of previous2 |
|  | Difference # ±5 % (preferably ± 3%)2 Regression slopes = 1.00 ± 0.03 and two intercepts are 0 ± 3 ppb2 |
| Trace-level NOy chemiluminscence3 | ± 15% span ± 3 ppb zero; 1/2-days level one2 |
|  | Multipoint calibration 0 and 4 upscale points ± 2% of full scale of best-fit straight line2 |
| Trace-level SO2 pulsed fluorescence3 | ± 15% span ± 0.8 ppb zero; 1/2-days level one2 |
|  | Multipoint calibration 0 and 4 upscale points ± 2% of full scale of best fit straight line2 |
| Trace-level CO NDIR-GFC3 | ± 15% span ± 0.05 ppm zero; 1/2-days level one2 |
|  | Multipoint calibration 0 and 4 upscale points ± 2% of full scale of best fit straight line2 |
| Wind Speed | Anemometer | ± 0.2 m/sec of actual wind speed at speeds < 5 m/sec |
|  |  | ± 5% of actual wind speed at speeds >= 5 m/sec |
| Wind Direction | Wind Vane | ± 3° C for each cardinal point |
| Relative Humidity | Thin film capacitor | ± 10% |
| Solar Radiation | Pyranometer | ± 5% of average solar radiation |
| Precipitation | Tipping Bucket Raingage | ± 0.02 inches at 0.50 inches of precipitation |
| Surface Wetness | Conductivity Bridge | Full-scale response to test resistance |
| Temperature | Platinum RTD | ± 0.3°C of actual temperature |
| Delta Temperature | Platinum RTD at 1 m and 10 m | ± 0.3°C of actual temperature |

1Ozone is measured at most CASTNET stations

2Quality Assurance Handbook Volume II: Part 1 (EPA-454/R-98-004)

3Gas trace-level measurements at select CASTNET stations, SOP available at http://www.epa.gov/castnet

Table 4. Assumed Number of Units for Bid

| CLIN | Description | Number of Units |
| --- | --- | --- |
|  |  | Base Period | Option Periods 1-4 |
|  |  | Minimum | Maximum | Minimum | Maximum |
| 1 | Core Operations | 1 | 1 | 1 | 1 |
| 2.1 | Dry deposition Filterpack - w/ operator | 46 | 52 | 0 | 100 |
| 2.2 | Dry deposition Filterpack - w/o operator | 8 | 8 | 0 | 0 |
| 3.1 | Ozone Monitoring - w/ operator | 38 | 44 | 0 | 100 |
| 3.2 | Ozone Monitoring - w/o operator | 5 | 5 | 0 | 0 |
| 4.1 | Ozone monitoring AQS - w/ operator | 8 | 8 | 0 | 100 |
| 4.2 | Ozone monitoring AQS - w/o operator | 3 | 3 | 0 | 0 |
| 5.1 | Meteorology - w/ operator | 46 | 52 | 0 | 100 |
| 5.2 | Meteorology - w/o operator | 8 | 8 | 0 | 0 |
| 6.1 | Trace gas NOy - w/ operator | 1 | 4 | 0 | 100 |
| 6.2 | Trace gas NOy - w/o operator | 1 | 6 | 0 | 0 |
| 7.1 | Trace gas SO2 - w/ operator | 1 | 4 | 0 | 100 |
| 7.2 | Trace gas SO2 - w/o operator | 1 | 6 | 0 | 0 |
| 8.1 | Trace gas CO - w/ operator | 1 | 4 | 0 | 100 |
| 8.2 | Trace gas CO - w/o operator | 1 | 6 | 0 | 0 |
| 9.1 | PM2.5 FRM mass - w/ operator | 0 | 0 | 0 | 100 |
| 9.2 | PM2.5 FRM mass - w/o operator | 0 | 0 | 0 | 0 |
| 10.1 | PM2.5 speciation - w/ operator | 0 | 0 | 0 | 100 |
| 10.2 | PM2.5 speciation - w/o operator | 0 | 0 | 0 | 0 |
| 11.1 | PM10-2.5 FRM mass - w/ operator | 0 | 0 | 0 | 100 |
| 11.2 | PM10-2.5 FRM mass - w/o operator | 0 | 0 | 0 | 0 |
| 12.1 | PM10-2.5 speciation - w/ operator | 0 | 0 | 0 | 100 |
| 12.2 | PM10-2.5 speciation - w/o operator | 0 | 0 | 0 | 0 |
| 13.1 | Continuous PM2.5 mass - w/ operator | 0 | 0 | 0 | 100 |
| 13.2 | Continuous PM2.5 mass - w/o operator | 0 | 0 | 0 | 0 |
| 14 | Filterpack prep & analysis | 4244 | 5168 | 0 | 7476 |
|  | Filterpack field samples | 3848 | 4680 | 0 | 6760 |
|  | Filterpack field blanks | 193 | 234 | 0 | 338 |
|  | Laboratory blanks | 193 | 234 | 0 | 338 |
|  | Artificial precipitation audit sample | 10 | 20 | 0 | 40 |
| 15.1 | Operation of NADP sampler - Collocated w/ filterpack | 12 | 20 | 0 | 30 |
| 15.2 | Operation of NADP sampler - Not collocated w/ filterpack | 3 | 10 | 0 | 30 |
| 16.1 | Operation of IMPROVE sampler - Collocated w/ filterpack | 2 | 5 | 0 | 10 |
| 16.2 | Operation of IMPROVE sampler - Not collocated w/ filterpack | 2 | 5 | 0 | 10 |
| 17 | Acquisition and Management of NPS data - | 20 | 30 | 0 | 30 |

Table 5. Analytical Methods and Minimum Detection Limits for Filter Extracts

| Analyte | Filter Media | Method | Minimum Reporting Limits1 | Method Detection Limit |
| --- | --- | --- | --- | --- |
| Ca2+ | Teflon® | EPA 6010B (ICP/AES) | 0.006 mg/L | 0.002 mg/L |
| Cl- | Teflon® | EPA 300.0 (IC) | 0.02 mg/L | 0.002 mg/L |
| K+ | Teflon® | EPA 6010B (ICP/AES) | 0.006 mg/L | 0.002 mg/L |
| Mg2+ | Teflon® | EPA 6010B (ICP/AES) | 0.003 mg/L | 0.001 mg/L |
| Na+ | Teflon® | EPA 6010B (ICP/AES) | 0.005 mg/L | 0.002 mg/L |
| NH4+ | Teflon® | EPA 350.1 (Automated Colorimetry) | 0.020 mg/L | 0.009 mg-N/L |
| NO3- | Teflon®, nylon, cellulose | EPA 300.0 (IC) | 0.008 mg-N/L | 0.003 mg/L |
| pH | (Precipitation only) | EPA 150.1 (pH meter) | 0.01 units | 0.01 units |
| SO42- | Teflon®, nylon, cellulose | EPA 300.0 (IC) | 0.040 mg/L | 0.015 mg/L |

1Determined as described in 40 CFR Part 136 Appendix B

Table 6. Acceptance Criteria for Quality Control Samples

| Quality Control Procedure | Acceptance Criteria |
| --- | --- |
| Calibration curve (minimum 5 points) correlation coefficient | > 0.995 |
| Calibration curve Y-intercept 95% Confidence Limit | < Reporting limits |
| Calibration curve responses | All samples must be within the standard calibration range. |
| Calibration Verification Standard | + 10% of true value for IC and ICP/AES analyses |
|  | + 10% of true value for AC (NH4+) analyses |
| Sample replicate | + 20% difference as compared to the initial sample run |
| Method blank | < 2x reporting limits |
| Reference sample | + 5% of true value for IC analyses |
|  | + 10% of true value for AC (NH4+) analyses |
| Filter blank | < 2x reporting limits |

Table 7. NADP Sites Collocated with CASTNET Sites

| NADP Site ID | Site Name, State | Collocated CASTNET Site ID |
| --- | --- | --- |
| VA24 | Prince Edward, VA | PED108 |
| TN04 | Speedwell, TN | SPD111 |
| OH54 | Deer Creek State Park, OH | DCP114 |
| MI52 | Ann Arbor, MI | ANA115 |
| WV05 | Cedar Creek State Park, WV | CDR119 |
| OH15 | Lykens, OH | LYK123 |
| MI51 | Unionville, MI | UVL124 |
| PA00 | Arendtsville, PA | ARE128 |
| WI35 | Perkinstown, WI | PRK134 |
| NC06 | Beaufort, NC | BFT142 |
| CT15 | Abington, CT | ABT147 |
| FL23 | Sumatra, FL | SUM156 |
| IL46 | Alhambra, IL | ALH157 |
| CO10 | Gothic, CO | GTH161 |
| AZ98 | Chiricahua, AZ | CHA467 |
| VA13 | Horton Station, VA | VPI120 |

Table 8. NADP Sites Requiring Site Operation Support

| NADP Site ID | Site Name, State |
| --- | --- |
| NC45 | Mt Mitchell, NC |
| CO94 | Sugarloaf, CO |
| WA21 | La Grande, WA |
| OR97 | Hylsop Farm, OR |
| GA20 | Bellville, GA |

Table 9. EPA IMPROVE Protocol Sites

| Database ID* | IMPROVE ID | Site Name | State |
| --- | --- | --- | --- |
| CTH510 | COHI1 | Connecticut Hill | NY |
| MKG513 | MKGO1 | M.K. Goddard | PA |
| ARE528 | AREN1 | Arendtville | PA |
| BVL530 | BOND1 | Bondville | IL |
| CDZ571 | CADI1 | Cadiz | KY |
| QAK572 | QUCI1 | Quaker City | OH |
| SIK570 | SIKE1 | Sikes | LA |
| LIV573 | LIVO1 | Livonia | IN |

* Site ID/designation based on CASTNET database.

# Text boxes

GTH161

HOW132

HOX148

HWF187

IRL141

SAN189

BEL116

CAT175

PAL190

KNZ184

LRL117

MCK131

MCK231

MKG113

OXF122

PND165

PNF126

PRK134

PSU106

ROM206

SAL133

SND152

STK138

SUM156

UVL124

VIN140

VPI120

ALC188

WSP144

WST109

ABT147

ALH157

ANA115

ARE128

ASH135

BFT142

BVL130

BWR139

CAD150

CDR119

CDZ171

CHE185

CKT136

CND125

CNT169

CON186

COW137

CTH110

CVL151

DCP114

EGB181

ESP127

GAS153