### Solar Orbiter

### High-Resolution Mission to the Sun and Inner Heliosphere

Assessment Study Report

# July  2000

# Foreword

The Solar Orbiter Mission was proposed to ESA by an international team of scientists led by E. Marsch in response to the call for mission proposals for two flexible missions (F2 and F3) and submitted on January 27, 2000. In March 2000 ESA's Space Science Advisory Committee recommended the Solar Orbiter for further study based on a pre-assessment study performed in 1999 in the framework of ESA’s Solar Physics Planning Group activities.

This document is the result of the “delta” assessment study, carried out by representatives of the European solar and heliospheric physics communities, in close co-operation with ESA staff.

Study team members:

E. Marsch, Max-Planck-Institut für Aeronomie,

Katlenburg-Lindau, Germany

E. Antonucci, Osservatorio Astronomico di Torino, Italy

P. Bochsler, University of Bern, Switzerland

J.-L. Bougeret,  Observatoire de Paris, Meudon, France

R. Harrison, Rutherford Appleton Laboratory, Chilton, UK

R. Schwenn, , Max-Planck-Institut für Aeronomie, Katlenburg-Lindau, Germany

J.-C. Vial, University of Paris XI, Orsay, France

# ESA staff members:

# Study Scientists:  	B. Fleck, ESA/GSFC, Greenbelt, Maryland, USA

# R. Marsden, ESA/ESTEC, Noordwijk, The Netherlands

# Study Manager:   	O. Pace, ESA/ESTEC, Noordwijk, The Netherlands

Solar System Mission Coordinator: M. Coradini, ESA HQ, Paris, France

Valuable contributions and comments on the science objectives and instrumentation were provided by:

M. Collados,  Instituto de Astrofisica de Canarias, Spain

C. Fröhlich, Physikalisch-Metorologisches Observatorium, Davos, Switzerland

L. Gizon, Stanford Univ., USA

B. Lites, High Altitude Observatory, Boulder, USA

O. von der Lühe,  Kieperheuer Institut für Sonnenphysik, Freiburg, Germany

V. Martinez Pillet,  Instituto de Astrofisica de Canarias, Spain

R.B. McKibben, Univ. of Chicago, USA

W. Schmidt,  Kieperheuer Institut für Sonnenphysik, Freiburg, Germany

V. Bothmer,  University of Kiel, Germany

R. Bruno,  Istituto Fisica Spazio Interplanetario del CNR, Roma, Italy

C. Chiuderi,  University of Florence, Italy

A. Cacciani,  University of Rome, Italy

L. Damé,  Service d' Aéronomie du CNRS, Verrières-le-Buisson, France

P. Hoyng,  SRON, Utrecht, The Netherlands

O. Kjeldseth-Moe,  University of Oslo, Norway

O. von der Lühe,  Kieperheuer Institut für Sonnenphysik, Freiburg, Germany

G. Mann,  Astrophysikalisches Institut Potsdam, Potsdam, Germany

V. Martinez Pillet,  Instituto de Astrofisica de Canarias, Spain

E. Priest,  University of St. Andrews, UK

W. Schmutz,  Physikalisch-Metorologisches Observatorium, Davos, Switzerland

S. Solanki, Max-Planck-Institut für Aeronomie, Lindau, Germany

J. Stenflo,  Eidgenössische Technische Hochschule Zürich, Switzerland

# Table of Contents

# Foreword

# 1. Executive Summary

# 2. Solar Orbiter Goals

# 3. Scientific Background

# 3.1 Status of the field and goals of Solar Orbiter

# 3.2 Key scientific objectives

# 3.2.1 Scientific rationale

# 3.2.2 Key goals for the near-Sun phase

# 3.2.3 Key goals for the out-of-ecliptic phase

# 3.3 Conclusions

# 4. Particles and Fields Environment

# 4.1 Microstate of the interplanetary solar wind

# 4.2 Solar wind ions as tracers of coronal structures

# 4.3 Magnetohydrodynamic turbulence

# 4.4 Acceleration and transport of solar energetic particles

# 4.5 Neutral particles from the Sun

# 4.6 Circumsolar and interplanetary dust

# 4.7 Solar neutrons

# 4.8 Solar radio emission

# 5. Morphology and activity of the Sun's magnetic field

# 5.1 Photospheric magnetic flux elements

# 5.2 Fine morphology and fast activity of coronal magnetic fields

# 6. Detailed links between the photosphere, corona and inner heliosphere

# 6.1 Global solar corona and solar wind

# 6.2 Structure of the magnetic network and origin of the solar wind

# 6.3 Waves in the corona

# 7. The Sun's polar regions and equatorial corona

# 7.1 The Sun's polar magnetic field and the dynamo

# 7.2 Coronal transients and their impact on the heliosphere

# 7.3 Solar luminosity variations

# 8. Scientific Payload

# 8.1 Measurement requirements

# 8.2 In-Situ Heliospheric Instruments

# 8.2.1 Solar Wind Plasma Analyser (SWA)

# 8.2.2 Plasma Waves Analyser (PWA)

# 8.2.3 Magnetometers (MAG)

# 8.2.4 Energetic Particle Detector (EPD)

# 8.2.5 Dust Detector (DUD)

# 8.2.6 Radio Instruments

# 8.2.7 Neutral Particle Detector (NPD)

# 8.3  Remote sensing solar instruments

# 8.3.1 General considerations

# 8.3.2 Visible-light imager and magnetograph (VIM)

# 8.3.3 EUV spectrometer (EUS)

8.3.4 EUV imager and X-ray imager (EXI)

# 8.3.5 Ultraviolet and visible-light coronagraph (UVC)

# 8.3.6 Neutron and (-ray detector (NGD)

# 8.3.7 Radiometer (RAD)

# 8.3.8 Other potential solar instruments

# 10. System Design

# 10.1 Design requirements and drivers

# 10.2 Main System Design Features

# 10.2.1 Requirements and Constraints

# 10.2.2 Spacecraft Baseline Design

# 10.2.3 Thruster Positioning

# 10.2.4 Thermal Design

# 10.2.5 Power Supply

# 10.3  Data Collection/Dumping

# 10.4  Radiation

# 10.5  Mass Budgets

# 11. Subsystem Design Description

# 11.1  Attitude and orbit control

# 11.2  Reaction Control System

# 11.3  Propulsion

# 11.4  Structure

# 11.5  Thermal C1ontrol

# 12. Ground Systems and Operations

# 12.1  Ground segment facilities and services

# 12.2  Ground Stations and Communications Network

# 12.3  Mission Control Centre

# 12.4  Computer facilities and Network

# 12.5  The Flight Control Software System

# 12.6  Mission Operations Concept

# 12.7  Scientific Operations

# 13. Management

13.1  F2/F3 Procurement Approach

13.2  Procurement Philosophy

13.3  Scientific Management and Instrument Selection

13.4  Industrial Management

13.5  Development Philosophy and Schedule

13.5.1 General

13.5.2 Payload Model Philosophy

13.5.3  Service Module Model Philosophy

13.5.4  Schedule

14. Bibliography

15. Mission and Spacecraft Summary