# PUBLIC PROPOSAL FORM

## FOR PUBLIC PROPOSALS ON THE INTERNATIONAL CODES

## 2003/2004 CODE DEVELOPMENT CYCLE

PLEASE SEE REVERSE FOR INSTRUCTIONS ON SUBMITTING PUBLIC PROPOSALS.  PROPOSALS MUST COMPLY WITH THESE INSTRUCTIONS.

CLOSING DATE: All Proposals Must Be Received by March 24, 2003.

- Indicate the format in which you would like to receive your Public Proposals Monograph (PPM), Report of the Hearing (ROH) and Final Action Agenda (FAA):

| x |  | Paper |  |  |  | * CD |  |  |  | *Download from ICC Website |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

(*Note: A paper copy will not be sent to you if you have chosen the CD or Download format.)

2)	PLEASE TYPE OR PRINT CLEARLY:  FORMS WILL BE RETURNED if they contain unreadable information.

| Name: | Ronald Majette | Date: | March 24, 2003 |
| --- | --- | --- | --- |
| Jurisdiction/Company: | U.S. Department of Energy |
| Submitted on Behalf of: | U.S. Department of Energy |
| Address: | 1000 Independence Avenue, EE-2J, 1J-018 |
| City: | Washington | State: | DC | Zip +4: | 20585 |
| Phone: | 202-586-7935 | Ext: |  | Fax: | 202-486-4617 |

| e-mail: | Ronald.Majette@hq.doe.gov |
| --- | --- |

| X | Signature on File |
| --- | --- |

3)	*Signature:

*I hereby grant the International Code Council the nonexclusive, royalty-free rights, including nonexclusive, royalty-free rights in copyright in this Proposal and I understand that I acquire no rights in any publication of International Code Council (ICC),  in which this Proposal in this or another similar analogous form is used.   I hereby attest that I have the authority and I am empowered to grant this copyright release.

| Indicate if this Proposal: |  |  |  | will |  | X |  | will not |  | increase the cost of construction. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

4)	Cost Impact:

IRC

5)	Indicate appropriate International Code(s) associated with this Public Proposal – Please use Acronym:

(See back of this form or the instructions for list of names and acronyms for the International Codes):

| 6) | Revision to: | x |  | Section | Various, Chap 11. |  |  |  | Table |  |  |  |  |  | Figure |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 7) | PROPOSAL | Please check appropriate box: |

|  |  | Revise as follows: |  |  |  | Add new text as follows |  | X |  | Delete and substitute as follows: |  |  |  | Delete without Substitution(s): |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Show the proposed NEW, REVISED or DELETED TEXT in legislative format: Line through text to be deleted. Underline text to be added.

Section R202

Delete “RESIDENTIAL BUILDING TYPE” without substitution.

Section R202

Revise the SUNROOM ADDITION definition.

SUNROOM ADDITION . A one-story structure added attached to an existing dwelling with a glazing area in excess of 40 percent of the gross area of the structure’s exterior walls and roof.

Section R202

Delete “THERMAL ISOLATION” and substitute:

THERMAL ISOLATION.  Physical and space conditioning separation from conditioned space(s). The conditioned space(s) shall be controlled as separate zones for heating and cooling or conditioned by separate equipment.

Section 318.1

Revise exception 3.

3. In counties identified with footnote a in Table N11011.2 as in climate zones 1 through 5 in Table N1101.2

R408.2

Delete all exceptions and add a new Section immediately following.

Unvented crawl space. Ventilation openings in under-floor spaces specified in Sections R408.1 and R408.2 shall not be required where:

- Exposed earth is covered with a continuous vapor retarder.  All joints of the vapor retarder shall overlap by 6 inches (153 mm) and shall be sealed or taped. The edges of the vapor retarder shall extend at least 6 inches (153 mm) up the stem wall and shall be attached to the stem wall,

- And one of the following is provided for the under-floor space:

  - Continuously operated mechanical exhaust ventilation at a rate equal to 1 cfm for each 20 ft2 of crawlspace floor area, or

  - Conditioned air supply sized to deliver at a rate equal to 1 cfm for each 20 ft2 of under-floor area, including a return pathway (such as a duct or transfer grille to the common area), and perimeter walls insulated in accordance with Section N1102.2.8, or

  - Plenum complying with M1601.4, if under floor spaces used as a plenum.

R806.4

Add new Section after R806.4

Conditioned attic assemblies: Unvented conditioned attic assemblies (spaces between the ceiling joists of the top story and the roof rafters) are permitted under the following conditions:

1.	No interior vapor retarders are installed on the ceiling side (attic floor) of the unvented attic assembly.

2.	An air-impermeable insulation is applied in direct contact to the underside/interior of the structural roof deck.  “Air-impermeable” shall be defined by ASTM E 283.

3.	In the warm humid locations as defined in N1101.2.1:

a. For asphalt roofing shingles: A 1 perm or less vapor retarder (determined using Procedure B of ASTM E 96) is placed to the exterior of the structural roof deck; i.e. just above the roof structural sheathing.

b. For wood shingles and shakes: a minimum continuous 1/4-inch air space separates the shingles/shakes and the roofing felt placed over the structural sheathing.

4.	In zones 3 through 8 as defined in N1101.2 sufficient insulation is installed to maintain the monthly average temperature of the condensing surface above 45°F. The condensing surface is defined as either the structural roof deck or the interior surface of an air-impermeable insulation applied in direct contact to the underside/interior of the structural roof deck. “Air-impermeable” is quantitatively defined by ASTM E 283.For calculation purposes, an interior temperature of 68°F is assumed. The exterior temperature is assumed to be the monthly average outside temperature.

R808.1

Revise.

Recessed lighting fixtures installed in the building thermal envelope shall meet the requirements of Section N1101.3 N1102.4.3.

# Delete Chapter 11 and substitute:

# CHAPTER 11

# Energy Efficiency

SECTION N1101

GENERAL

N1101.1 Scope. This chapter regulates the energy efficiency for the design and construction of buildings regulated by this code.

Exception: Portions of the building envelope that do not enclose conditioned space.

N1101.2 Compliance. Compliance shall be demonstrated by either meeting the requirement of the International Energy Conservation Code or meeting the requirements of this chapter.  Climate zones from Table N1101.2 shall be used in determining the applicable requirements from this chapter.

N1101.2.1 Warm humid counties.  Warm humid counties are listed in Table N1101.2.1.

N1101.3 Identification. Materials, systems and equipment shall be identified in a manner that will allow a determination of compliance with the applicable provisions of this chapter.

N1101.4 Building thermal envelope insulation. An R-value identification mark shall be applied by the manufacturer to each piece of building thermal envelope insulation 12 inches (305 mm) or greater in width. Alternately, the insulation installers shall provide a certification listing the type, manufacturer and R-value of insulation installed in each element of the building thermal envelope. For blown or sprayed insulation, the initial installed thickness, settled thickness, settled R-value, installed density, coverage area and number of bags installed shall be listed on the certification. The insulation installer shall sign, date and post the certification in a conspicuous location on the job site.

N1101.4.1 Blown or sprayed roof/ceiling insulation. The thickness of blown in or sprayed roof/ceiling insulation shall be written in inches on markers that are installed at least one for every 300 ft2 (28 m2) throughout the attic space. The markers shall be affixed to the trusses or joists and marked with the minimum initial installed thickness with numbers a minimum of 1 inch (25 mm) in height. Each marker shall face the attic access opening.

N1101.4.2 Insulation mark installation. Insulating materials shall be installed such that the manufacturer’s R-value mark is readily observable upon inspection.

Table N1101.5.

Default Glazed Fenestration U-Factors

| Frame Type | Single Pane | Double Pane | Skylight |
| --- | --- | --- | --- |
|  |  |  | Single | Double |
| Metal | 1.20 | 0.80 | 1.60 | 1.05 |
| Non-Metal or metal clad | 0.95 | 0.55 | 1.25 | 0.80 |
| Glazed Block | 0.60 |

N1101.5 Fenestration product rating. U-factors of fenestration products (windows, doors and skylights) shall be determined in accordance with NFRC 100 by an accredited, independent laboratory, and labeled and certified by the manufacturer. Products lacking such a labeled U-factor shall be assigned a default U-factor from Table N1101.5.  The solar heat gain coefficient (SHGC) of glazed fenestration products (windows, glazed doors and skylights) shall be determined in accordance with NFRC 200 by an accredited, independent laboratory, and labeled and certified by the manufacturer. Products lacking such a labeled SHGC shall be assigned a default SHGC of 0.75 for single pane and 0.65 for double pane and glazed block.

N1101.6 Installation. All materials, systems and equipment shall be installed in accordance with the manufacturer’s installation instructions and the conditions of any listing or required certifications.

Figure N1101.2.  Climate Zones

Table N1101.2     CLIMATE ZONES BY STATE AND COUNTY

Alabama

Zone 3 except

Zone 2

Baldwin

Mobile

Alaska

Zone 7 except

Zone 8

Bethel

Dellingham

Fairbanks North Star

Nome

North Slope

Northwest Arctic

Southeast Fairbanks

Wade Hampton

Yukon-Koyukuk

Arizona

Zone 3 except

Zone 2

La Paz

Maricopa

Pima

Pinal

Yuma

Zone 4

Gila

Yavapai

Zone 5

Apache

Coconino

Navajo

Arkansas

Zone 3 except

Zone 4

Baxter

Benton

Boone

Carroll

Fulton

Izard

Madison

Marion

Newton

Searcy

Stone

Washington

California

Zone 3 Dry except

Zone 2

Imperial

Zone 3 Marine

Alameda

Marin

Mendocino

Monterey

Napa

San Benito

San Francisco

San Luis Obispo

San Mateo

Santa Barbara

Santa Clara

Santa Cruz

Sonoma

Ventura

Zone 4 Dry

Amador

Calaveras

El Dorado

Inyo

Lake

Mariposa

Trinity

Tuolumne

Zone 4 Marine

Del Norte

Humboldt

Zone 5

Lassen

Modoc

Nevada

Plumas

Sierra

Siskiyou

Zone 6

Alpine

Mono

Colorado

Zone 5 except

Zone 4

Baca

Las Animas

Otero

Zone 6

Alamosa

Archuleta

Chaffee

Conejos

Costilla

Custer

Dolores

Eagle

Moffat

Ouray

Rio Blanco

Saguache

San Miguel

Zone 7

Clear

Creek

Grand

Gunnison

Hinsdale

Jackson

Lake

Mineral

Park

Pitkin

Rio Grande

Routt

San Juan

Summit

Connecticut

Zone 5

Delaware

Zone 4

Dist Of Columbia

Zone 4

Florida

Zone 2 except

Zone 1

Broward

Dade

Monroe

Georgia

Zone 3 except

Zone 2

Appling

Atkinson

Bacon

Baker

Berrien

Brantley

Brooks

Bryan

Camden

Charlton

Chatham

Clinch

Colquitt

Cook

Decatur

Echols

Effingham

Evans

Glynn

Grady

Jeff Davis

Lanier

Liberty

Long

Lowndes

McIntosh

Miller

Mitchell

Pierce

Seminole

Tattnall

Thomas

Toombs

Ware

Wayne

Zone 4

Banks

Catoosa

Chattooga

Dade

Dawson

Fannin

Floyd

Franklin

Gilmer

Gordon

Habersham

Hall

Lumpkin

Murray

Pickens

Rabun

Stephens

Towns

Union

Walker

White

Whitfield

Hawaii

Zone 1

Idaho

Zone 6 except

Zone 5

Ada

Benewah

Canyon

Cassia

Clearwater

Elmore

Gem

Gooding

Idaho

Jerome

Kootenai

Latah

Lewis

Lincoln

Minidoka

Nez Perce

Owyhee

Payette

Power

Shoshone

Twin Falls

Washington

Illinois

Zone 5 except

Zone 4

Alexander

Bond

Christian

Clay

Clinton

Crawford

Edwards

Effingham

Fayette

Franklin

Gallatin

Hamilton

Hardin

Jackson

Jasper

Jefferson

Johnson

Lawrence

Macoupin

Madison

Marion

Massac

Monroe

Montgomery

Perry

Pope

Pulaski

Randolph

Richland

Saline

Shelby

St Clair

Union

Wabash

Washington

Wayne

White

Williamson

Indiana

Zone 5 except

Zone 4

Brown

Clark

Crawford

Daviess

Dearborn

Dubois

Floyd

Gibson

Greene

Harrison

Jackson

Jefferson

Jennings

Knox

Lawrence

Martin

Monroe

Ohio

Orange

Perry

Pike

Posey

Ripley

Scott

Spencer

Sullivan

Switzerland

Vanderburgh

Warrick

Washington

Iowa

Zone 5 except

Zone 6

Allamakee

Black Hawk

Bremer

Buchanan

Buena Vista

Butler

Calhoun

Cerro Gordo

Cherokee

Chickasaw

Clay

Clayton

Delaware

Dickinson

Emmet

Fayette

Floyd

Franklin

Grundy

Hamilton

Hancock

Hardin

Howard

Humboldt

Ida

Kossuth

Lyon

Mitchell

O’Brien

Osceola

Palo Alto

Plymouth

Pocahontas

Sac

Sioux

Webster

Winnebago

Winneshiek

Worth

Wright

Kansas

Zone 4 except

Zone 5

Cheyenne

Cloud

Decatur

Ellis

Gove

Graham

Greeley

Hamilton

Jewell

Lane

Logan

Mitchell

Ness

Norton

Osborne

Phillips

Rawlins

Republic

Rooks

Scott

Sheridan

Sherman

Smith

Thomas

Trego

Wallace

Wichita

Kentucky

Zone 4

Louisiana

Zone 2 except

Zone 3

Bienville

Bossier

Caddo

Caldwell

Catahoula

Claiborne

Concordia

De Soto

East Carroll

Franklin

Grant

Jackson

La Salle

Lincoln

Madison

Morehouse Natchitoches

Ouachita

Red River

Richland

Sabine

Tensas

Union

Vernon

Webster

West Carroll

Winn

Maine

Zone 6 except

Zone 7

Aroostook

Maryland

Zone 4 except

Zone 5  Garrett

Massachusetts

Zone 5

Michigan

Zone 5 except

Zone 6

Alcona

Alger

Alpena

Antrim

Arenac

Benzie

Charlevoix

Cheboygan

Clare

Crawford

Delta

Dickinson

Emmet

Gladwin

Grand Traverse

Huron

Iosco

Isabella

Kalkaska

Lake

Leelanau

Manistee

Marquette

Mason

Mecosta

Menominee

Missaukee

Montmorency

Newaygo

Oceana

Ogemaw

Oscoda

Otsego

Presque Isle

Roscommon

Sanilac

Wexford

Zone 7

Baraga

Chippewa

Gogebic

Houghton

Iron

Keweenaw

Luce

Mackinac

Ontonagon

Schoolcraft

Minnesota

Zone 6 except

Zone 7

Aitkin

Becker

Beltrami

Carlton

Cass

Clay

Clearwater

Cook

Crow Wing

Grant

Hubbard

Itasca

Kanabec

Kittson

Koochiching

Lake Of The Woods Mahnomen

Marshall

Mille Lacs

Norman

Otter Tail

Pennington

Pine

Polk

Red Lake

Roseau

St Louis

Wadena

Wilkin

Mississippi

Zone 3 except

Zone 2

Hancock

Harrison

Jackson

Pearl River

Stone

Missouri

Zone 4 except

Zone 5

Adair

Andrew

Atchison

Buchanan

Caldwell

Chariton

Clark

Clinton

Daviess

De Kalb

Gentry

Grundy

Harrison

Holt

Knox

Lewis

Linn

Livingston

Macon

Marion

Mercer

Nodaway

Pike

Putnam

Ralls

Schuyler

Scotland

Shelby

Sullivan

Worth

Montana

Zone 6

Nebraska

Zone 5

Nevada

Zone 5 except

Zone 3

Clark

New Hampshire

Zone 6 except

Zone 5

Cheshire

Hillsborough

Rockingham

Strafford

New Jersey

Zone 4 except

Zone 5

Bergen

Hunterdon

Mercer

Morris

Passaic

Somerset

Sussex

Warren

New Mexico

Zone 4 except

Zone 3

Chaves

Dona Ana

Eddy

Hidalgo

Lea

Luna

Otero

Zone 5

Catron

Cibola

Colfax

Harding

Los Alamos

McKinley

Mora

Rio Arriba

San Juan

San Miguel

Sandoval

Santa Fe

Taos

Torrance

New York

Zone 5 except

Zone 4

Bronx

Kings

Nassau

New York

Queens

Richmond

Suffolk

Westchester

Zone 6

Allegany

Broome

Cattaraugus

Chenango

Clinton

Delaware

Essex

Franklin

Fulton

Hamilton

Herkimer

Jefferson

Lewis

Madison

Montgomery

Oneida

Otsego

Schoharie

Schuyler

St Lawrence

Steuben

Sullivan

Tompkins

Ulster

Warren

Wyoming

North Carolina

Zone 3 except

Zone 4

Alamance

Alexander

Bertie

Buncombe

Burke

Caldwell

Caswell

Catawba

Chatham

Cherokee

Clay

Cleveland

Davie

Durham

Forsyth

Franklin

Gates

Graham

Granville

Guilford

Halifax

Harnett

Haywood

Henderson

Hertford

Iredell

Jackson

Lee

Lincoln

Macon

Madison

McDowell

Nash

Northampton

Orange

Person

Polk

Rockingham

Rutherford

Stokes

Surry

Swain

Transylvania

Vance

Wake

Warren

Wilkes

Yadkin

Zone 5

Alleghany

Ashe

Avery

Mitchell

Watauga

Yancey

North Dakota

Zone 7 except

Zone 6

Adams

Billings

Bowman

Burleigh

Dickey

Dunn

Emmons

Golden Valley

Grant

Hettinger

La Moure

Logan

McIntosh

McKenzie

Mercer

Morton

Oliver

Ransom

Richland

Sargent

Sioux

Slope

Stark

Ohio

Zone 5 except

Zone 4

Adams

Brown

Clermont

Gallia

Hamilton

Lawrence

Pike

Scioto

Washington

Oklahoma

Zone 3 Moist except

Zone 4 Dry

Beaver

Cimarron

Texas

Oregon

Zone 4 Marine except

Zone 5 Dry

Baker

Crook

Deschutes

Gilliam

Grant

Harney

Hood River

Jefferson

Klamath

Lake

Malheur

Morrow

Sherman

Umatilla

Union

Wallowa

Wasco

Wheeler

Pennsylvania

Zone 5 except

Zone 4

Bucks

Chester

Delaware

Montgomery

Philadelphia

York

Zone 6

Cameron

Clearfield

Elk

McKean

Potter

Susquehanna

Tioga

Wayne

Rhode Island

Zone 5

South Carolina

Zone 3

South Dakota

Zone 6 except

Zone 5

Bennett

Bon Homme

Charles Mix

Clay

Douglas

Gregory

Hutchinson

Jackson

Mellette

Todd

Tripp

Union

Yankton

Tennessee

Zone 4 except

Zone 3

Chester

Crockett

Dyer

Fayette

Hardeman

Hardin

Haywood

Henderson

Lake

Lauderdale

Madison

McNairy

Shelby

Tipton

Texas

Zone 2 Moist except

Zone 2 Dry

Bandera

Dimmit

Edwards

Kinney

La Salle

Maverick

Medina

Real

Uvalde

Val Verde

Webb

Zapata

Zavala

Zone 3 Dry

Andrews

Baylor

Borden

Brewster

Callahan

Childress

Coke

Coleman

Collingsworth

Concho

Cottle

Crane

Crockett

Crosby

Culberson

Dawson

Dickens

Ector

El Paso

Fisher

Foard

Gaines

Garza

Glasscock

Hall

Hardeman

Haskell

Hemphill

Howard

Hudspeth

Irion

Jeff Davis

Jones

Kent

Kerr

Kimble

King

Knox

Loving

Lubbock

Lynn

Martin

Mason

Mcculloch

Menard

Midland

Mitchell

Motley

Nolan

Pecos

Presidio

Reagan

Reeves

Runnels

Schleicher

Scurry

Shackelford

Sterling

Stonewall

Sutton

Taylor

Terrell

Terry

Throckmorton

Tom Green

Ward

Wheeler

Wilbarger

Winkler

Zone 3 Moist

Archer

Blanco

Bowie

Brown

Burnet

Camp

Cass

Clay

Collin

Comanche

Cooke

Dallas

Delta

Denton

Eastland

Ellis

Erath

Fannin

Franklin

Gillespie

Grayson

Gregg

Hamilton

Harrison

Henderson

Hood

Hopkins

Hunt

Jack

Johnson

Kaufman

Kendall

Lamar

Lampasas

Llano

Montague

Stephens

Wichita

Wise

Young

Marion

Mills

Morris

Nacogdoches

Navarro

Palo

Pinto

Panola

Parker

Rains

Red

River

Rockwall

Rusk

Sabine

San Augustine

San Saba

Shelby

Smith

Somervell

Tarrant

Titus

Upshur

Van Zandt

Wood

Zone 4

Armstrong

Bailey

Briscoe

Carson

Castro

Cochran

Dallam

Deaf Smith

Donley

Floyd

Gray

Hale

Hansford

Hartley

Hockley

Hutchinson

Lamb

Lipscomb

Moore

Ochiltree

Oldham

Parmer

Potter

Randall

Roberts

Sherman

Swisher

Yoakum

Utah

Zone 5 except

Zone 3

Washington

Zone 6

Box Elder

Cache

Carbon

Daggett

Duchesne

Morgan

Rich

Summit

Uintah

Wasatch

Vermont

Zone 6

Virginia

Zone 4

Washington

Zone 4 Marine except

Zone 5 Dry

Adams

Asotin

Benton

Chelan

Columbia

Douglas

Franklin

Garfield

Grant

Kittitas

Klickitat

Lincoln

San Juan

Skamania

Spokane

Walla Walla

Whitman

Yakima

Zone 6 Dry

Ferry

Okanogan

Pend

Oreille

Stevens

West Virginia

Zone 5 except

Zone 4

Berkeley

Boone

Braxton

Cabell

Calhoun

Clay

Gilmer

Jackson

Jefferson

Kanawha

Lincoln

Logan

Mason

McDowell

Mercer

Mingo

Monroe

Morgan

Pleasants

Putnam

Ritchie

Roane

Tyler

Wayne

Wirt

Wood

Wyoming

Wisconsin

Zone 6 except

Zone 7

Ashland

Bayfield

Burnett

Douglas

Florence

Forest

Iron

Langlade

Lincoln

Oneida

Price

Sawyer

Taylor

Vilas

Washburn

Wyoming

Zone 6 except

Zone 5

Goshen

Platte

Zone 7

Lincoln

Sublette

Teto

Table N1101.2.1 Warm Humid Counties.

Alabama

Autauga

Baldwin

Barbour

Bullock

Butler

Choctaw

Clarke

Coffee

Conecuh

Covington

Crenshaw

Dale

Dallas

Elmore

Escambia

Geneva

Henry

Houston

Lowndes

Macon

Marengo

Mobile

Monroe

Montgomery

Perry

Pike

Russell

Washington

Wilcox

Arkansas

Columbia

Hempstead

Lafayette

Little River

Miller

Sevier

Union

Florida

All

Georgia

All in Zone 2

Plus

Ben Hill

Bleckley

Bulloch

Calhoun

Candler

Chattahoochee

Clay

Coffee

Crisp

Dodge

Dooly

Dougherty

Early

Emanuel

Houston

Irwin

Jenkins

Johnson

Laurens

Lee

Macon

Marion

Montgomery

Peach

Pulaski

Quitman

Randolph

Schley

Screven

Stewart

Sumter

Taylor

Telfair

Terrell

Tift

Treutlen

Turner

Twiggs

Webster

Wheeler

Wilcox

Worth

Louisiana

All in Zone 2

Plus

Bienville

Bossier

Caddo

Caldwell

Catahoula

Claiborne

Concordia

De Soto

Franklin

Grant

Jackson

La Salle

Lincoln

Madison

Natchitoches

Ouachita

Red River

Richland

Sabine

Tensas

Union

Vernon

Webster

Winn

Mississippi

All in Zone 2

Plus

Adams

Amite

Claiborne

Copiah

Covington

Forrest

Franklin

George

Greene

Hinds

Jefferson

Jefferson Davis

Jones

Lamar

Lawrence

Lincoln

Marion

Perry

Pike

Rankin

Simpson

Smith

Walthall

Warren

Wayne

Wilkinson

North Carolina

Brunswick

Carteret

Columbus

New Hanover

Onslow

Pender

South Carolina

Allendale

Bamberg

Barnwell

Beaufort

Berkeley

Charleston

Colleton

Dorchester

Georgetown

Hampton

Horry

Jasper

Texas

All in Zone 2

Plus

Blanco

Bowie

Brown

Burnet

Camp

Cass

Collin

Comanche

Dallas

Delta

Denton

Ellis

Erath

Franklin

Gillespie

Gregg

Hamilton

Harrison

Henderson

Hood

Hopkins

Hunt

Johnson

Kaufman

Kendall

Lamar

Lampasas

Llano

Marion

Mills

Morris

Nacogdoches

Navarro

Palo

Pinto

Panola

Parker

Rains

Red

River

Rockwall

Rusk

Sabine

San Augustine

San Saba

Shelby

Smith

Somervell

Tarrant

Titus

Upshur

Van Zandt

Wood

N1101.6.1 Protection of exposed foundation insulation. Insulation applied to the exterior of foundation walls and the perimeter of slab-on-grade floors shall have a rigid, opaque and weather-resistant protective covering to prevent the degradation of the insulation’s thermal performance. The protective covering shall cover the exposed exterior insulation and extend a minimum of 6 inches (153 mm) below grade. N1101.7 Above code programs.  The building official or other authority having jurisdiction shall be permitted to deem a national, state or local energy efficiency program to exceed the energy efficiency required by this chapter. Buildings approved in writing by such an energy efficiency program shall be considered in compliance with this chapter.

N1101.8 Certificate.  A permanent certificate shall be posted inside the building on the electrical distribution panel.  The certificate shall be completed by the builder or registered design professional.  The certificate shall list the predominant R-values of insulation installed in or on ceiling/roof, walls, foundation (slab, basement wall, crawlspace wall and/or floor) and ducts outside conditioned spaces; U-factors for fenestration; and, where requirements apply, the solar heat gain coefficient (SHGC) of fenestration.  Where there is more than one value for each component, the certificate shall list the value covering the largest area.  The certificate shall list the type and efficiency of heating, cooling and service water heating equipment.

SECTION N1102

BUILDING THERMAL ENVELOPE

N1102.1 Insulation and fenestration criteria.

The building thermal envelope shall meet the requirements of Table N1102.1 based on the climate zone specified in Table N1102.1.

N1102.1.1 R-value computation.  Insulation material used in layers, such as framing cavity insulation and insulating sheathing, shall be summed to compute the component R-value.  The manufacturer’s settled R-value shall be used for blown insulation.  Computed R-values shall not include an R-value for other building materials or air films.

N1102.1.2 U-factor alternative.  An assembly with a U-factor equal to or less than that specified in Table N1102.1.2 shall be permitted as an alternative to the R-value in Table N1102.1.

N1102.2Total UA alternative. If the total building thermal envelope UA (sum of U-factor times assembly area) is less than or equal to the total UA resulting from using the U-factors in Table N1102.1.2, the building shall be considered in compliance with Table N1102.1.  The UA calculation shall be done using a method consistent with the ASHRAE Handbook of Fundamentals and shall include the thermal bridging effects of framing materials.  The SHGC requirements shall be met in addition to UA compliance.

N1102.1.4 Prescriptive trade offs.  The trade offs specified in Table N1102.1.4 shall be permitted as an alternative to Table N1102.1.

N1102.2 Specific insulation requirements.

N1102.2.1 Ceilings with attic spaces.  When Section N1102.1 would require R-38 in the ceiling, R-30 shall be deemed to satisfy the requirement for R-38 wherever the full height of uncompressed R-30 insulation extends over the wall top plate at the eaves.  Similarly R-38 shall be deemed to satisfy the requirement for R-49 wherever the full height of uncompressed R-38 insulation extends over the wall top plate at the eaves.

N1102.2.2 Ceilings without attic spaces.  Where Section N1102.1 would require insulation levels above R-30 and the design of the roof/ceiling assembly does not allow sufficient space for the required insulation, the minimum required insulation for such roof/ceiling assemblies shall be R-30.

N1102.2.3 Mass walls.  Mass walls for the purposes this chapter shall be considered walls of concrete block, concrete, insulated concrete form (ICF), masonry cavity, brick (other than brick veneer), earth (adobe, compressed earth block, rammed earth), and solid timber/logs.  The provisions of Section N1102.1 for mass walls shall be applicable when at least 50% of the required insulation R-value is on the exterior of, or integral to, the wall. Walls that do not meet this criterion for insulation placement shall meet the wood frame wall insulation requirements of Section N1102.1.

N1102.2.4 Steel-frame ceilings, walls and floors. Steel-frame ceilings, walls and floors shall meet the insulation requirements of Table N1102.2.4 or shall meet the wall U-factor requirements in Table N1102.1.2.  The calculation of the U-factor for a steel-frame wall shall use a series-parallel path calculation method.

N1102.2.5 Floors.  Floor insulation shall be installed to maintain permanent contact with the underside of the subfloor decking.

N1102.2.6 Basement walls.  Walls associated with conditioned basements shall be insulated from the top of the basement wall down to 10 feet below grade or to the basement floor, whichever is less. Walls associated with unconditioned basements shall meet this requirement unless the floor overhead is insulated in accordance with Sections N1102.1 and N1102.2.5.

N1102.2.7 Slab-on-grade floors.  Slab-on-grade floors with a floor surface less than 12 inches below grade shall be insulated in accordance with Table N1102.1.  The insulation shall extend downward from the top of the slab on the outside or inside of the foundation wall.  Insulation located below grade shall be extended the distance provided in Table N1102.1 by any combination of vertical insulation, insulation extending under the slab or insulation extending out from the building.  Insulation extending away from the building shall be protected by pavement or by a minimum of 10 inches of soil.  The top edge of the insulation installed between the exterior wall and the edge of the interior slab shall be permitted to be cut at a 45-degree angle away from the exterior wall. Slab-edge insulation is not required in jurisdictions designated by the code official as having a very heavy termite infestation.

N1102.2.8 Crawl space walls.  As an alternative to insulating floors over crawl spaces, crawl space walls shall be permitted to be insulated when the crawl space is not vented to the outside.  Crawl space wall insulation shall be permanently fastened to the wall and extend downward from the floor to the finished grade level and then vertically and/or horizontally for at least an additional 24 inches (610 mm). Exposed earth in unvented crawl space foundations shall be covered with a continuous vapor retarder.  All joints of the vapor retarder shall overlap by 6 inches (153 mm) and be sealed or taped. The edges of the vapor retarder shall extend at least 6 inches (153 mm) up the stem wall and shall be attached to the stem wall.

N1102.2.9 Masonry veneer.  Insulation shall not be required on the horizontal portion of the foundation that supports a masonry veneer.

N1102.2.10 Thermally isolated sunroom insulation. The minimum ceiling insulation R-values shall be R-19 in zones 1 through 4 and R-24 in zones 5 though 8.  The minimum wall R-value shall be R-13 in all zones. New wall(s) separating the sunroom from conditioned space shall meet the building thermal envelope requirements.

N1102.3 Fenestration.

N1102.3.1 U-factor.  An area-weighted average of fenestration products shall be permitted to satisfy the U-factor requirements.

N1102.3.2 Glazed fenestration SHGC.  An area-weighted average of fenestration products more than 50% glazed shall be permitted to satisfy the SHGC requirements.

N1102.3.3 Glazed fenestration exemption.  Up to 15 ft2 of glazed fenestration per dwelling unit shall be permitted to be exempt from U-factor and SHGC requirements in Section N1102.1.

N1102.3.4 Opaque door exemption.  One opaque door assembly is exempted from the U-factor requirement in Section N1102.1.

N1102.3.5 Thermally isolated sunroom U-factor. For zones 4 through 8 the maximum fenestration U-factor shall be 0.50 and the maximum skylight U-factor shall be 0.75. New windows and doors separating the sunroom from conditioned space shall meet the building thermal envelope requirements.

N1102.3.6 Replacement fenestration.  Where some or all of an existing fenestration unit is replaced with a new fenestration product, including frame, sash, and glazing, the replacement fenestration unit shall meet the applicable requirements for U-factor and SHGC in Table N1102.1.

N1102.3.7 Impact resistant fenestration.  Jurisdictions in zones 1 through 4 that require impact resistant fenestration that meets ASTM E-1886, ASTM E-1996, or other approved impact standard shall be exempt from the fenestration U-factor requirement. Fenestration so exempted shall be listed and labeled by the manufacturer as meeting the approved impact standard.

N1102.4 Air leakage.

N1102.4.1 Building thermal envelope.  The building thermal envelope shall be durably sealed to limit infiltration.  The sealing methods between dissimilar materials shall allow for differential expansion and contraction.  The following shall be caulked, gasketed, weatherstripped or otherwise sealed with an air barrier material, suitable film or solid material.

- All joints, seams and penetrations.

- Site-built windows, doors and skylights.

- Openings between window and door assemblies and their respective jambs and framing.

- Utility penetrations.

- Dropped ceilings or chases adjacent to the thermal envelope.

- Knee walls.

- Walls and ceilings separating the garage from conditioned spaces.

- Behind tubs and showers on exterior walls.

- Common walls between dwelling units.

10. Other sources of infiltration.

N1102.4.2 Fenestration air leakage. Windows, skylights and sliding-glass doors shall have an air infiltration rate of no more than 0.3 cfm/ft2, and swinging doors no more than 0.5 cfm/ft2, when tested according to NFRC 400, 101/I.S.2, or 101/I.S.2/NAFS by an accredited, independent laboratory, and listed and labeled by the manufacturer.

Exemptions:  Site-built windows, skylights and doors.

N1102.4.3 Recessed lighting. Recessed lighting fixtures installed in the building thermal envelope shall be sealed to limit air leakage between conditioned and unconditioned spaces by being:

- IC-rated and labeled with enclosures that are sealed or gasketed to prevent air leakage to the ceiling cavity or unconditioned space; or

- IC-rated and labeled as meeting ASTM E 283 when tested at 1.57 psi (75 Pa) pressure differential with no more than 2.0 cfm (0.944 L/s) of air movement from the conditioned space to the ceiling cavity; or

- located inside an airtight sealed box with clearances of at least 0.5 inches (12.7 mm) from combustible material and 3 inches (76mm) from insulation.

N1102.5 Moisture control. The building design shall not create conditions of accelerated deterioration from moisture condensation.  Frame walls, floors and ceilings not ventilated to allow moisture to escape shall be provided with an approved vapor retarder. The vapor retarder shall be installed on the warm-in-winter side of the thermal insulation.

Exceptions:

- In construction where moisture or its freezing will not damage the materials.

- Frame walls, floors and ceilings in jurisdictions in Zones 1 through 5. (Crawl space floor vapor retarders are not exempted.)

- Where other approved means to avoid condensation are provided.

N1102.5.1 Maximum fenestration U-factor.  The maximum fenestration U-factor permitted using trade offs from Section N1102.1.3 in zones 6 through 8 shall be 0.55.

SECTION N1103

SYSTEMS

N1103.1 Controls.  At least one thermostat shall be provided for each separate heating and cooling system.

N1103.2 Ducts.

N1103.2.1 Insulation.  Supply and return ducts shall be insulated to a minimum of R-8. Ducts in floor trusses shall be insulated to a minimum of R-6.

Exception:  Ducts or portions thereof located completely inside the building thermal envelope or within the building thermal envelope and separated from the exterior of the building thermal envelope with at least R-8 insulation.

N1103.2.2 Sealing.  All ducts, air handlers, filter boxes, and building cavities used as ducts shall be sealed.   Joints and seams shall comply with M1601.3.1.

N1103.2.3 Building cavities.  Building framing cavities shall not be used as supply ducts.

N1103.3 Mechanical system piping insulation.  Mechanical system piping capable of carrying fluids above 105 F or below 55 F shall be insulated to a minimum of R-2.

N1103.4 Circulating hot water systems.  All circulating service hot water piping shall be insulated to at least R-2.  Circulating hot water systems shall include an automatic or readily accessible manual switch that can turn off the hot water circulating pump when the system is not in use.

N1103.5 Mechanical ventilation.  Outdoor air intakes and exhausts shall have automatic or gravity dampers that close when the ventilation system is not operating.

N1103.6 Equipment sizing.  Heating and cooling equipment shall be sized as specified in M1401.3.

Add new to Section M1303.1

5. Maintenance instructions. Required regular maintenance actions. Title or publication number for the operation and maintenance manual for that particular model and type of product.

6. Equipment efficiency. Equipment efficiency for heating, cooling and service water heating equipment with equipment efficiency regulated as an AFUE, HSPF, SEER or EF.

Exception: Equipment assembled in the field.

Section AJ102.4.

Replacement windows.  Regardless of the category of work, when an entire existing window, including frame, sash and glazed portion is replaced, the replacement window shall comply with the requirements of Section 1102.4 Chapter 11.

### Table N1102.1.  Insulation and Fenestration Requirements by Component(a)

| Climate Zone | Fenestration U-Factor | Skylight(b) U-Factor | Glazed Fenestration SHGC | Ceiling R-Value | Wood Frame Wall R-Value | Mass Wall R-Value | Floor R-Value | Basement(c) Wall R-Value | Slab(d) R-Value & Depth | Crawl Space(c) Wall R-Value |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1.20 | 1.60 | 0.40 | 30 | 13 | 6 | 13 | 0 | 0 | 0 |
| 2 | 0.80 | 1.05 | 0.40 | 30 | 13 | 6 | 13 | 0 | 0 | 0 |
| 3 | 0.60 | 0.90 | 0.40(e) | 30 | 13 | 6 | 19 | 0 | 0 | 5/13 |
| 4 except Marine | 0.40 | 0.60 | NR | 38 | 13 | 8 | 19 | 10 / 13 | 10, 2 ft | 10 / 13 |
| 5 and Marine 4 | 0.35 | 0.60 | NR | 38 | 19 or 13+5(g) | 13 | 25(f) | 10 / 13 | 10, 2 ft | 10 / 13 |
| 6 | 0.35 | 0.60 | NR | 49 | 19 or 13+5(g) | 15 | 30(f) | 10 / 13 | 10, 4 ft | 10 / 13 |
| 7 and 8 | 0.35 | 0.60 | NR | 49 | 21 | 21 | 30(f) | 15 / 21 | 15, 4 ft | 10 / 13 |
| (a) R-values are minimums. U-factors and SHGC are maximums. R-19 shall be permitted to be compressed into a 2x6 cavity. (b) The fenestration U-factor column excludes skylights. The SHGC column applies to all glazed fenestration. (c) The first R-value applies to continuous insulation, the second to framing cavity insulation; either insulation meets the requirement. (d) R-5 shall be added to the required slab edge R-values for heated slabs. (e) There are no SHGC requirements in the Marine zone. (f) Or insulation sufficient to fill the framing cavity, R-19 minimum. (g) “13+5” means R-13 cavity insulation plus R-5 insulated sheathing. If structural sheathing covers 25% or less of the exterior, R-5 sheathing is not required where structural sheathing is used. If structural sheathing covers more than 25% of exterior, structural sheathing shall be supplemented with insulated sheathing of at least R-2. |

### Table N1102.1.2.  Equivalent U-Factors(a)

| Climate Zone | Fenestration U-Factor | Skylight U-Factor | Ceiling U-Factor | Frame Wall U-Factor | Mass Wall U-Factor | Floor U-Factor | Basement Wall U-Factor | Crawl Space Wall U-Factor |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1.20 | 1.60 | 0.035 | 0.082 | 0.110 | 0.064 | 0.360 | 0.477 |
| 2 | 0.80 | 1.05 | 0.035 | 0.082 | 0.110 | 0.064 | 0.360 | 0.477 |
| 3 | 0.60 | 0.90 | 0.035 | 0.082 | 0.110 | 0.047 | 0.360 | 0.136 |
| 4 except Marine | 0.40 | 0.60 | 0.030 | 0.082 | 0.099 | 0.047 | 0.059 | 0.065 |
| 5 and Marine 4 | 0.35 | 0.60 | 0.030 | 0.060 | 0.082 | 0.037 | 0.059 | 0.065 |
| 6 | 0.35 | 0.60 | 0.026 | 0.060 | 0.077 | 0.033 | 0.059 | 0.065 |
| 7 and 8 | 0.35 | 0.60 | 0.026 | 0.057 | 0.057 | 0.033 | 0.041 | 0.057 |
| (a) Non-fenestration U-factors shall be obtained from measurement, calculation or an approved source. |

Table N1102.2.4.  Steel-Frame Ceiling, Wall and Floor Insulation (R-Value)

| Wood Frame R-Value Requirement | Cold-Formed Steel Equivalent R –Value1 |
| --- | --- |
| Steel Truss Ceilings2 |
| R-30 | R-38 or R-30+3 or R-26+5 |
| R-38 | R-49 or R-38+3 |
| R-49 | R-38+5 |
| Steel Joist Ceilings2 |
| R-30 | R-38 in 2x4 or 2x6 or 2x8 R-49 in any framing |
| R-38 | R-49 in 2x4 or 2x6 or 2x8 or 2x10 |
| Steel Framed Wall |
| R-13 | R-13+5 or R-15+4 or R-21+3 |
| R-19 | R-13+9 or R-19+8 or R-25+7 |
| R-21 | R-13+10 or R-19+9 or R-25+8 |
| Steel Joist Floor |
| R-13 | R-19 in 2x6 R-19+R6 in 2x8 or 2x10 |
| R-19 | R-19+R-6 in 2x6 R-19+R-12 in 2x8 or 2x10 |
| Notes: 1. Cavity insulation R-value is listed first, followed by continuous insulation R-value. 2. Insulation exceeding the height of the framing shall cover the framing. |

Table N1102.1.4.  HVAC System Tradeoffs

| Climate Zone(s) | Required Improvement for HVAC System | Allowed Alternatives for Insulation/Fenestration1 |
| --- | --- | --- |
| 2 | SEER 13 OR Ducts & HVAC in conditioned space OR Ground source heat pump | Any fenestration U-factor |
| 3 | SEER 13 with AFUE 90 OR SEER 13 with HSPF 7.9 OR Ducts & HVAC in conditioned space OR Ground source heat pump | Double pane window with any U-factor |
| 4 or 5 | SEER 12 with AFUE 92 OR SEER 12 with HSPF 8.2 OR Ducts & HVAC in conditioned space OR Ground source heat pump | R-0 unconditioned basement R-0 slab R-19 floor |
| 5 | SEER 12 with AFUE 92 OR SEER 12 with HSPF 8.2 OR Ducts & HVAC in conditioned space OR Ground source heat pump | R-13 wall R-19 floor |
| 6 | SEER 12 with AFUE 92 OR SEER 12 with HSPF 8.2 OR Ducts & HVAC in conditioned space OR Ground source heat pump | R-38 ceiling R-13 wall |
| 7 | AFUE 92 OR HSPF 8.2 OR Ducts & HVAC in conditioned space OR Ground source heat pump | R-38 ceiling R-15 wall |
| Notes: Table N1102.1 requirements not stated remain the same. All footnotes of Table N1102.1 apply. After the year 2006 the SEER shall be increased by 2 from the value in this table; HSPF shall increase from 7.9 to 8.5 and from 8.2 to 8.8. In zones 3 through 8 dwelling units with electric resistance heating are not eligible to use this table. “Ducts & HVAC in conditioned space” includes air-handler and furnace being in conditioned space. Factory-sealed air handlers tested, listed and labeled by the manufacturer as having a 2% or less leakage rate at 1.0 inch water gauge shall meet the requirement for air handler being in conditioned space. For the uninsulated unconditioned basements trade off in Zones 4 and 5, at most one foot of the basement wall can be above grade. Any combination of the foundation insulation specified shall be permitted. Slabs with uninsulated hot water pipes, uninsulated air distribution ducts or electric heating cables installed within or under the slab are not eligible for this tradeoff of slab-edge insulation. Evaporative cooling shall meet the SEER requirement if code official has deemed evaporative cooling appropriate to the climate of the jurisdiction. Marine zone residences without mechanical air conditioning shall be exempt from the SEER requirement in this table. |

8)	SUPPORTING INFORMATION (State purpose and reason, and provide substantiation to support proposed change):

The purpose of this proposal to the International Residential Code [IRC]) and to the International Energy Conservation Code is to further the usability of the energy codes.  The U.S. Department of Energy has for the past decade worked to promote the energy codes in numerous ways—assisting states and localities in adopting and implementing IECC/IRC-based codes, developing and deploying user-friendly code compliance tools, hosting workshops and training sessions, operating an energy codes hotline, assembling and distributing information via a dedicated web site and email list, and proposing helpful changes to the IECC through the ICC code development process.  Directly parallel and usually identical changes are being proposed for the IECC.

As DOE has promoted the adoption and use of the IRC/IECC, builders and code officials have repeatedly echoed one consistent comment—that the residential portion of the IECC/IRC is difficult to understand, complicated to adopt and implement, and expensive to enforce.  This comment has been widespread in spite of the availability of very easy-to-use—and free—code compliance software.  In evaluating the causes for these comments, DOE has identified a number of specific characteristics that make the energy portion of the IRC and residential IECC difficult to use, especially by jurisdictions with limited staff and budget.  In no particular order, these include:

- Because IECC thermal criteria (insulation and windows requirements) are a function of heating degree-days (HDD), and any particular location may have multiple sources of HDD data or be equally distant from more than one source, there is sometimes ambiguity as to what the code requires.  Further, the HDD framework makes it difficult to properly accommodate cooling concerns in the code.  Finally, the HDD basis, which is used only in some of the IECC’s compliance paths, differs from the county-defined zones used in some other compliance paths (including some commercial sections) of the IECC and in the IRC.

- Because envelope stringency is a function of glazing area as a percentage of wall area, the code behaves irrationally in some ways.  For example, the code tends to permit a less efficient envelope for larger houses and for houses with inefficient aspect ratios or ceiling heights.  In apparent contradiction, low-window-area homes (e.g., low-budget starter homes) can have wall and window requirements that are unreasonably inefficient.

- The IRC has energy requirements only for residences with glazing less than 15%, making it an incomplete energy code.

- The code’s requirements are very non-uniform, especially in the IECC, making it difficult or impossible for builders and code officials (and homebuyers) to develop a sense of the code’s baseline requirements in a jurisdiction.  For example, the HDD-based requirements vary from location to location within a jurisdiction, and often result in unexpected differences between adjacent jurisdictions that are part of a larger community or metropolitan area.  Further, because envelope efficiency requirements vary with building geometry, the code’s requirements cannot be known until a design is finalized, which makes change orders after construction has begun difficult and expensive, sometimes resulting in noncompliance even when the new design would use less energy.  Also, different building types generally have different requirements.  Finally, the combination of HDD-based criteria and county-based zones results in apparent ambiguities and sometimes jurisdictional confusion between residential and commercial sections.

- The IECC code text is frequently cited as being difficult to read and understand due to its length and apparent lack of integration between compliance paths.

For all the reasons listed above, DOE finds that enforcement of the code is inconsistent at best, and very rare for some important building elements such as glazing area, which has a large influence on the required R-values and U-factors for a given house.

DOE has therefore developed a proposal that rewrites Chapter 11 of the IRC and residential sections of the IECC.  The intent is to transform the code to a format that is easy to understand, easy for builders and inspectors to remember, relatively unchanging within jurisdictional boundaries, unambiguous, and inexpensive to adopt and enforce.  The format we have chosen is exemplified by a single provision that was introduced to the IECC in 1998—the SHGC requirement for windows in southern locations.  That code provision, in contrast to the bulk of the code, has been well understood, readily implemented, and has generated little if any confusion.  DOE’s current code change proposal follows that model in several ways, focusing on clear and unambiguous specifications even at the expense of some precision.  (The SHGC requirement is a uniform 0.40 over a very large geographical area and never changes regardless of the building type, size, shape, orientation, or any other factor.)

This code change reformats the IRC’s energy provisions without substantially affecting the overall stringency of the code.  Note, however, that with any change in format, especially one that changes the geo-climatic basis for the requirements, some specific locations will experience modest stringency changes.

Another goal of this proposal is to produce efficiency prescriptions that are easily memorized by builders and code officials in any particular jurisdiction, as codes of this nature are observed to experience considerably higher compliance rates than codes for which each and every house has different requirements.  Despite its historical length and complexity, the IECC actually has provisions for only a handful of residential energy efficiency measures—primarily the building envelope components and HVAC distribution systems.  DOE’s primary intent is to provide very simple, clear, and fair requirements for these measures.

Following the philosophy discussed above, DOE’s change proposal has the following major characteristics:

- The climate basis of the proposed requirements has been changed from simple HDD to geographical zones that are based on multiple climate variables (so that both heating and cooling considerations are accommodated).  Further, within the U.S., the zones are completely defined by political boundaries (county lines) so that code users will never have to choose from disparate climate data sources to determine local requirements.  The proposed new climate zones were developed in an open process, in consultation with relevant standards committees of the American Society of Heating Refrigerating, and Air Conditioning Engineers (ASHRAE).  The proposed zones are designed to be an appropriate foundation for both residential and commercial codes, and may be useful in other contexts as well.  A thorough discussion of the zones’ development can be found at http://www.energycodes.gov/implement/pdfs/climate_paper_review_draft_rev.pdf

- The proposed code changes prescriptive envelope requirements are not a function of window area.  Eliminating this dependency has a number of beneficial effects on the code’s usability and enforceability.  DOE has analyzed the potential drawbacks of this approach and has concluded that the benefits outweigh them.  This analysis is available for review at http://www.energycodes.gov/implement/pdfs/wwr_elimination.pdf

- The proposed code change is designed to accommodate local practices and preferences, eliminating common local hurdles to code compliance.  For example, the proposal accommodates some coastal regions’ need for glazing with high wind ratings and high-termite regions’ need for easy compliance without slab-edge insulation.

- The proposed code change is designed to increase consumer awareness of a home’s energy features, by making baseline requirements more uniform within a jurisdiction and by requiring a disclosure of each house’s R-values, U-factors, and HVAC efficiencies.

- The proposed code change is designed, to the extent practicable, to incorporate aspects of the latest building science regarding energy efficiency and its effects on moisture control and durability.  For example, the proposed code change contains provisions related to unvented crawlspaces, modifies vapor retarder requirements, requires sealing of air handlers in garages, and limits worst-case glazing U-factors in locations where moisture condensation can be a serious problem.

- The proposed IECC code change greatly simplifies and streamlines the text, eliminates unused definitions, brings other definitions into agreement with those in other ICC codes, and eliminates many inadvertent loopholes that have resulted from unintended interactions between compliance paths.

In preparing this change proposal, DOE has worked for two years with numerous interested parties, including builders, code officials, manufacturers, efficiency advocates, energy simulation experts, and building scientists.  DOE has worked openly, making successive drafts of the change proposal available for review via DOE’s energy codes web site (http://www.energycodes.gov/).  Over one hundred individuals and entities provided hundreds of helpful comments.  DOE reviewed all comments carefully and tried to craft a proposal that fairly balances all viewpoints without compromising the overall goal of increased usability.  Parts of the proposal were developed in consultation with experts from ASHRAE’s 90.1 standard committee.

DOE believes this proposed change, if adopted, will result in a much easier to use code, easier and hence more widespread adoption of IRC / IECC-based state codes, easier and less expensive enforcement, and more consistent compliance even in jurisdictions with minimal enforcement infrastructure.  We urge the ICC to consider this proposal on those merits.

PLEASE USE SEPARATE FORM FOR EACH PROPOSAL

SUBMITTAL AS A DOCUMENT ATTACHMED TO AN E-MAIL IS PREFERRED

(SEE REVERSE FOR DIRECTIONS ON WHERE TO SEND PROPOSALS)