Chemical Storage

Storage  According to Hazard Classes

The following guidelines are provided for the safe storage of hazardous materials in accordance with their hazard classes:

Consult the EH&S Chemical Safety Web Page for additional guidance. This contains Material Safety Data Sheet and toxicological databases.  An EH&S Industrial Hygienist can also be consulted, if additional assistance is needed.

Acids

o Segregate acids from reactive metals such as sodium, potassium, magnesium, etc.

o Segregate oxidizing acids from organic acids, flammable and combustible materials.

o Segregate acids from chemicals which could generate toxic or flammable gases upon contact, such as sodium cyanide, iron sulfide, calcium carbide, etc.

o Segregate acids from bases.

o See Control Procedures for Acids and Bases.

Bases

o Segregate bases from acids, metals, explosives, organic peroxides and easily ignitable materials.

o See Control Procedures for Acids and Bases.

Solvents (Flammable and Halogenated Solvents)

o Store in approved safety cans or cabinets.

o Segregate from oxidizing acids and oxidizers.

o Keep away from any source of ignition:  heat, sparks, or open flames.

o See Control Procedures for Flammable and Combustible Liquids.

Oxidizers

o Store in a cool, dry place.

o Keep away from combustible and flammable materials.

o Keep away from reducing agents such as zinc, alkali metals, and formic acid.

Cyanides

o Segregate from acids and oxidizers.

Water Reactive Chemicals

o Store in a cool, dry place away from any water source.

o Make certain that a Class D fire extinguisher is available in case of fire.

o See Control Procedures for Water Reactive Chemicals.

Pyrophoric Substance

o (Materials which will react with the air to ignite when exposed, e.g., white phosphorus.)

o Store in a cool, dry place making provisions for an airtight seal.

Light Sensitive Chemicals

o Store in amber bottles in a cool, dry, dark place.

Peroxide Forming Chemicals

o Store in airtight containers in a dark, cool, and dry place.

o Label containers with receiving, opening, and disposal dates.

o Periodically test for the presence of peroxides.

o See Control Procedures for Peroxide Forming Compounds.

Toxic Chemicals

o Store according to the nature of the chemical, using appropriate security where necessary.

Incompatible Chemicals

Certain hazardous chemicals should not be mixed or stored with other chemicals because a severe reaction can take place or an extremely toxic reaction product can result. The label and MSDS will contain information on incompatibilities.

The following incompatibility matrix and table contains examples of incompatible chemicals:

Know the properties of the chemicals used.

The chemical incompatibilities discussed below are by no means exhaustive.  As a result, it is important for laboratory personnel to thoroughly research the properties of the chemicals they are using.  Material Safety Data Sheets (MSDSs) have sections on chemical incompatibility.  The container's label should also provide storage guidelines.

Avoid mixing incompatible waste materials.

A number of serious laboratory accidents have occurred when people have poured incompatible waste materials into hazardous waste containers.  Use separate waste containers for each type of waste.  Consult an EH&S Waste Generator Specialist for guidance.

Store incompatible chemicals separately.

Common storage problems in laboratories can lead to mixing incompatible chemicals.  The most serious of these is the storage of acids (especially oxidizing acids) with flammable solvents.  Contact of a concentrated oxidizing acid with a flammable solvent would likely result in a fire or an explosion.  This is not an unlikely scenario in the event of an earthquake.  Storage of chemicals in alphabetical order on shelves often results in incompatible chemicals being stored together.  For example, alphabetical arrangement could result in hydrogen peroxide (a strong oxidizer) being stored next to hydrazine (a very strong reducer).

| CHEMICAL | KEEP OUT OF CONTACT WITH |
| --- | --- |
| Acetic Acid | Chromic acid, nitric acid, hydroxyl compounds, ethylene glycol, perchloric acid, peroxides, permanganates |
| Acetone | Concentrated nitric and sulfuric acid mixtures, and strong bases |
| Acetylene | Chlorine, bromine, copper, fluorine, silver, mercury |
| Alkali Metals | Water, carbon tetrachloride or other chlorinated hydrocarbons, carbon dioxide, the halogens |
| Ammonia, anhydrous | Mercury, chlorine, calcium hypochlorite, iodine, bromine, hydrofluoric acid |
| Ammonium Nitrate | Acids, metal powders, flammable liquids, chlorates, nitrites, sulfur, finely divided organic or combustible materials |
| Aniline | Nitric acid, hydrogen peroxide |
| Arsenic materials | Any reducing agent |
| Azides | Acids |
| Bromine | Same as chlorine |
| Calcium Oxide | Water |
| Carbon (activated) | Calcium hypochlorite, all oxidizing agents |
| Carbon tetrachloride | Sodium |
| Chlorates | Ammonium salts, acids, metal powders, sulfur, finely divided organic or combustible materials |
| Chromic Acid and Chromium trioxide | Acetic acid, naphthalene, camphor, glycerol, glycerin, turpentine, alcohol, flammable liquids in general |
| Chlorine | Ammonia, acetylene, butadiene, butane, methane, propane (or other petroleum gases), hydrogen, sodium carbide, turpentine, benzene, finely divided metals |
| Chlorine Dioxide | Ammonia, methane, phosphine, hydrogen sulfide |
| Copper | Acetylene, hydrogen peroxide |
| Cumene Hydroperoxide | Acids, organic or inorganic |
| Cyanides | Acids |
| Flammable Liquids | Ammonium nitrate, chromic acid, hydrogen peroxide, nitric acid, sodium peroxide, halogens |
| Hydrocarbons | Fluorine, chlorine, bromine, chromic acid, sodium peroxide |
| Hydrocyanic Acid | Nitric acid, alkali |
| Hydrofluoric Acid | Ammonia, aqueous or anhydrous |
| Hydrogen Peroxide | Copper, chromium, iron, most metals or their salts, alcohols, acetone, organic materials, aniline, nitromethane, flammable liquids |
| Hydrogen Sulfide | Fuming nitric acid, other acids, oxidizing gases, acetylene, ammonia (aqueous or anhydrous), hydrogen |
| Hypochlorites | Acids, activated carbon |
| Iodine | Acetylene, ammonia (aqueous or anhydrous), hydrogen |
| Mercury | Acetylene, fulminic acid, ammonia |
| Nitrates | Sulfuric acid |
| Nitric Acid (concentrated) | Acetic acid, aniline, chromic acid, hydrocyanic acid, hydrogen sulfide, flammable liquids, flammable gases, copper, brass, any heavy metals |
| Nitrites | Acids |
| Nitroparaffins | Inorganic bases, amines |
| Oxalic Acid | Silver, mercury |
| Oxygen | Oils, grease, hydrogen; flammable liquids, solids, or gases |
| Perchloric Acid | Acetic anhydride, bismuth and its alloys, alcohol, paper, wood, grease and oils |
| Peroxides, organic | Acids (organic or mineral), avoid friction, store cold |
| Potassium | Carbon tetrachloride, carbon dioxide, water |
| Potassium chlorate and perchlorate | Sulfuric and other acids |
| Potassium Permanganate | Glycerin, ethylene glycol, benzaldehyde, sulfuric acid |
| Selenides | Reducing agents |
| Sodium nitrite | Ammonium nitrate and other ammonium salts |
| Sodium Peroxide | Ethyl or methyl alcohol, glacial acetic acid, acetic anhydride, benzaldehyde, carbon disulfide, glycerin, ethylene glycol, ethyl acetate, methyl acetate, furfural |
| Sulfides | Acids |
| Sulfuric Acid | Potassium chlorate, potassium perchlorate, potassium permanganate (or compounds with similar light metals, such as sodium, lithium, etc.) |
| Tellurides | Reducing agents |

From Manufacturing Chemists' Association, Guide for Safety in the Chemical Laboratory,  pp. 215-217, Van Nostrand Reinhold, 2nd Edition.