MEMORANDUM							August 13, 2003

Subject:		Triethylene Glycol, PC Code 083501.  Product Chemistry Science Chapter for the Reregistration Eligibility Decision (RED) Process (Case # 3146)

From:			A. Najm Shamim, Ph.D., Chemist

Regulatory Management Branch II

Antimicrobials Division (7510C)

To:			Ben Chambliss, Acting Team Leader

Regulatory Management Branch II

Antimicrobials Division (7510C)

Thru:			Connie Welch, Chief

Regulatory Management Branch II

Antimicrobials Division (7510C)

Enclosed is the Product chemistry Science Chapter for Tiethylene Glycol for consideration of the Reregistration Eligibility Decision (RED).

Common Name:		Triethylene Glycol

CAS#:				112-27-6

Chemical Name:		1,2-Bis(hydroxyethoxy)ethane

Molecular Formula:		C6H14O4

Color:				Colorless

Odor:				Odorless

B.P.				285 o C, ( at 760 mm Hg) 165 o C at 14 mm Hg.

M.P.				- 5 o C (- 7 o C)1

Molecular Weight:		150.20 g/mol

Specific Gravity:		1.1274

Solubility:			Highly miscible in water

Soluble in alcohol, benzene, toluene, sparingly soluble in ether and insoluble in petroleum ether

Vapor Pressure:		< 0.01 mm Hg at 20 o C (0.00132 mm Hg at 25 o C)1

Dissociation Constant:	Contains no hydrolysable protons.

pH:				6- 9.5

Log Kow :			-1.741

Flammability:			~ 150 o C

Explodability:			n/a: Product is not explosive

Stability:			Stable at normal temperatures of use and staorage

Storage Stability:		n/a: Product is not an MP or EP

Viscosity:			39.4 cPs at 22 o C

Miscibility:			n/a: product is not an MP or EP with use directions: to dilute with petroleum solvents.

Corrosion Characteristics:	Should be kept in inert container

Oxidizing or Reducing:	n/a: Product does not contain any oxidizing or reducing agents.

Dielectric Breakdown

Voltage: 			n/a product is not an EP for use in/on/around electrical equipment.

Structure:

OH-CH2-CH2-O-CH2-CH2-O-CH2-CH2-OH

References

USEPA, 2003. “EPA Estimation of Physical/Chemical Properties Program” Http://www.epa.gv/oppt/exposure/docs/episuitedl.htm

42814401		Davis, K. (1993) Product Chemistry Data of Triethylene Glycol: Lab Project Number: TEG61. Unpublished study prepared by RegWest Co.6 p.

42814402		Davis, K. (1993) Product Chemistry Data of Triethylene Glycol: Lab Project Number: TEG62. Unpublished study prepared by RegWest Co.

13 p.

42814403		Davis, K. (1993) Physical & Chemical Characteristics of Triethylene Glycol: Lab Project Number: TEG63. Unpublished study prepared by RegWest Co. 91 p.