SPACECRAFT DESIGN

and

MISSION OPERATIONS

SNAP  ORBIT

- "Prometheus" Orbit Baselined Following Preliminary Trade Study

- Uses Lunar Assist to Achieve a 19 X 57 Re Orbit with a Delta III 8930 Launch Vehicle

- Good Overall Optimization of Mission Trade-offs

- Low Earth Albedo Provides Multiple Advantages:

- Facilitates Passive Cooling of Detectors

- Minimizes Stray Light in Telescope

- Minimum Thermal Change on Structure Reduces Demand on ACS

- Good Visibility from Berkeley Ground Station

- Outside Radiation Belts

- Orbit Reachable with Available Launch Vehicle

SPACECRAFT DESCRIPTION

- Detailed Spacecraft Design will be Done in Collaboration with Teaming Partner

- Intent of System Design is to:

- Keep Interfaces as Well Defined and Simple as Possible

- Utilize Experience and Strengths of Team Members

- Spacecraft System is Comprised of Four Major Functional Blocks

- Power System

- Propulsion/ACS System

- Telecommunications System

- Observatory Control Unit

POWER SYSTEM

- Two 1 Square Meter Arrays of GaAs Cells Supply 340 Watts at End of Life

- Arrays Fold Out after Launch and Lock in Place

- Gimbaling of Arrays is Not Required

- Controller Performs Battery Charge Management and Power Distribution Function

TELECOMMUNICATIONS SYSTEM

- S-Band Transponder with Two Low Gain Antennas Provides Uplink and Emergency Downlink

- X-Band Transmitter with 25 Watt Traveling Wave Tube Amplifier and 50 cm Steered Antenna Provides 50 megabit per second Link to Berkeley Ground Station

POINTING  STRATEGY

- Telescope Pointing Task is Broken into Two Parts

- Conventional 3 Axis Pointing System on Spacecraft Gives Accuracy of 2 Arc-seconds in 3 Axes

- Accomplished Using Mid to High End Conventional Components

- Requires Careful Attention be Paid to Structure Stiffness and Damping

- Stand Alone System on Spacecraft will be Spec'ed to Required Accuracy

- Fast Steering Mirror System Augments Pointing Provided by Spacecraft to Achieve Required .03 Arc-second Pointing of Telescope

- Roll Axis Accuracy of Spacecraft System is OK

- Fast Tracking Mirror Corrects 2 Cross Axes

- The Two Systems are Completely Independent

- No Exchange of Control Signals as on NGST

ACS/PROPULSION SYSTEM

- Strawman Design Provides Pointing Control on Spacecraft to 2 Arc Seconds

- Two Ball CT 602 Star Trackers

- Reaction Wheel Package Uses Ithaco Type B 16 nms Wheels with Special Balancing

- IMU Package Comprised of Litton Hemispheric Resonator Gyros

- Dedicated Controller Separate from Data System

- This Accuracy is Adequate for Science Mission in Roll Axis

- Requirement on Cross Axis Pointing Effectively Met with Fast Steering Mirror in Telescope

ACS/PROPULSION SYSTEM  (continued)

- Propulsion System Uses Mono Propellant Hydrazine

- Single 10 Newton Main Engine

- Redundant Set of Six 1 Newton Attitude Control Engines

- System Dry Mass is 15 kg

- 49 kg Fuel Capacity

- 25 kg Needed for Apogee Adjust

- 5 kg Allocated for Navigation

- 5 kg Allocated for Reaction Wheel Management

- 14 kg Margin

OBSERVATORY CONTROL UNIT

- Primary Task is Receipt of High Rate Telemetry from Payload and Transfer to Downlink

- Receives and Processes Ground Commands

- Controls Other Spacecraft Systems

- Collects Engineering Telemetry and Performs Observatory Thermal Control

- Performs Initial Acquisition and Spacecraft Safing Functions

SPACECRAFT STRUCTURE

- Careful Attention to Structure Design Essential to Meeting Requirements on ACS System

- Delta III Fairing Allows Separate Structure for  Payload and Spacecraft

- Math Modeling will be Done on the Combined Payload and Spacecraft Structure

LAUNCH VEHICLE

- Boeing Delta III 8930 will Deliver >2800 kg to Prometheus Orbit

- Spacecraft Propulsion System Used for Mid-course Correction and Apogee Reduction

- Fairing will Accommodate All Telescope Designs Under Consideration

OBSERVATORY INTEGRATION and TESTING

- Large and Complex Task Requires Carefully Developed Plan

- Detailed I&T Plan will be Developed During Study Phase

- Current Test Philosophy Includes:

- Build Test Functions into Hardware

- Perform System Level Tests as Early as Possible

- e.g. Do Subsystem Interface Tests at Bread Board Level

- Test End-to-End Whenever Possible

- Ability to Support Tests is an Important Factor in Choice of Teaming Partners

- Strawman Plans Include:

- Optics Testing Done by Optics Subcontractor

- Spacecraft Contractor will Deliver a Fully Tested Spacecraft

- Mechanical and Electrical Integration will be Done in the SSL High Bay

- Observatory Vibration and T/V Done in a Bay Area Facility

- Final End-to-End Optical Test will be Done in an Appropriate Facility

MISSION OPERATIONS

- Mission Operations Center (MOC) at Space Sciences Using Berkeley Ground Station

- Fully Automated System Tracks Multiple Spacecraft

- Science Operations Center (SOC) at Lawrence Berkeley Laboratory Built Around NERSC Super Computer

- Multiple Terabytes Data Storage

- High Speed Links to CPU Farms & Supercomputers

- Intensive Processing Done on Supercomputer with Final Analysis on PC's

OR

- Grand Challenge-like Software System

- Operations are Based on a Four Day Period

- Autonomous Operation of the Spacecraft

- Coincident SOC Review of Data with Build of Next Target List

- Upload Instrument Configuration for Next Period