417-R-SEISSPORD-0030

Geostationary Operational Environmental Satellite

(GOES)

GOES-R Series

Space Environment In-Situ Suite (SEISS)

Performance and Operational Requirements Document (PORD)

Baseline Version 1.0

7/12/04

1.	Scope	1

1.1.	Identification	1

1.2.	Mission Review	1

1.3.	Document Overview	1

1.4.	Terminology	2

1.5	Definitions	2

1.6	Requirement Applicability	3

2.	Applicable Documents	3

3.	Sensor Requirements	3

3.1.	Sensor Definition	3

3.1.1.	SEISS Modes	3

3.1.2.1	Safe Mode	4

3.1.2.2	Normal Operational Mode	4

3.1.2.3	Instrument Diagnostic Mode	4

3.1.2.	On-Orbit Operations	4

3.1.2.1.	Reserved	5

3.1.2.2.	Reserved	5

3.1.2.3.	Eclipse	5

3.1.2.4.	Operations After Maneuvers	5

3.1.2.4.1.	Yaw Flip	5

3.1.2.4.2.	Stationkeeping	5

3.1.2.5.	Activation	5

3.1.2.6.	On-Orbit Storage	5

3.2.	Sensor Requirements	5

3.2.1.	General Requirements	5

3.2.1.1.	Noise	5

3.2.1.2.	Stability	5

3.2.1.3.	In-Flight Calibration	6

3.2.1.4.	Ground Calibration	6

3.2.1.5.	Out-of-Band Response	6

3.2.2.	MPS Requirements	6

3.2.2.1.	Low Energy Electrons and Protons	6

3.2.2.1.1.	Flux Measurement Range	6

3.2.2.1.2.	Accuracy	6

3.2.2.1.3.	Spatial Coverage and Field of View	6

3.2.2.1.4.	Data Rate	6

3.2.2.1.5.	Maximum and Minimum Flux	7

3.2.2.2.	Medium and high energy electrons and protons	7

3.2.2.2.1.	Measurement Range	7

3.2.2.2.2.	Accuracy	7

3.2.2.2.3.	Spatial Coverage and Field of View	7

3.2.2.2.4.	Data Rate	8

3.2.2.2.5.	Maximum and Minimum Flux	8

3.2.3.	SGPS Requirements	8

3.2.3.1.	Measurement Range	8

3.2.3.2.	Accuracy	9

3.2.3.3.	Spatial Coverage and Field of View	9

3.2.3.4.	Data Rate	9

3.2.3.5.	Minimum and Maximum Flux	9

3.2.4.	EHIS Requirements	9

3.2.4.1.	Measurement Range	9

3.2.4.2.	Accuracy	10

3.2.4.3.	Spatial Coverage and Field of View	10

3.2.4.4.	Data Rate	10

3.2.4.5.	Minimum and Maximum Flux	10

3.3.	Design Requirements	10

3.3.1.	Reliability	10

3.3.2.	Mechanical Requirements	11

3.3.2.1.	Design Limit Loads	11

3.3.2.2.	Non-Linear Loads	11

3.3.2.3.	Yield Strength	11

3.3.2.4.	Ultimate Strength	11

3.3.2.5.	Structural Stiffness	11

3.3.2.6.	Unit Stiffness	12

3.3.2.7.	Material Properties	12

3.3.2.8.	Critical Members Design Values	12

3.3.2.9.	Redundant Members Design Values	12

3.3.2.10.	Selective Design Values	12

3.3.2.11.	Structural Reliability	12

3.3.2.12.	Mechanisms	13

3.3.2.13.	Pressurized Units	13

3.3.2.14.	Alignment Reference	14

3.3.3.	Thermal Requirements	14

3.3.3.1.	Temperature Limits	14

3.3.3.2.	Non Operational Temperature	14

3.3.3.3.	Thermal Control Hardware	14

3.3.4.	On-Board Processor Requirements	14

3.3.4.1.	Flight Load Non-volatile Memory	14

3.3.4.2.	Commandable Reinitialization	14

3.3.4.3.	Deterministic Power-on Configuration	14

3.3.4.4.	Fail-safe Recovery Mode	14

3.3.5.	Flight Software Requirements	15

3.3.5.1.	Language and Methodology	15

3.3.5.2.	Software Module Upload	15

3.3.5.3.	Flexibility and Ease of Software Modification	15

3.3.5.4.	Version Identifiers	15

3.3.5.5.	Flight Processor Resource Sizing	15

3.3.5.6.	Software Event Logging	16

3.3.5.7.	Warm Restart	16

3.3.5.8.	Memory Tests	16

3.3.5.9.	Memory Dump	16

3.3.5.10.	Telemetry	16

3.3.6.	Power Requirements	17

3.3.6.1.	Power Regulators and Supplies	17

3.3.6.2.	Fuses	17

3.3.6.3.	Test Connectors	17

3.3.7.	Magnetic Properties	17

3.3.8.	Spacecraft Level Ground Testing	17

3.3.9.	Ground Support Equipment and Development Facilities	17

3.3.9.1.	Electrical System Test Equipment	17

3.3.9.2.	Flight Software Development Environment	18

3.3.9.3.	Shipping Container	18

4.	Acronyms	18

# Scope

## Identification

This Performance and Operational Requirements Document (PORD) sets forth the performance requirements for the National Oceanic and Atmospheric Administration (NOAA) Space Environment In-Situ Suite (SEISS).

## Mission Review

The SEISS particle sensors shall monitor the proton, electron, and heavy ion fluxes at geosynchronous orbit.  These particle fluxes roughly consist of three components:  1) a geomagnetically trapped and highly variable population of electrons and protons; 2) sporadic fluxes of electrons, protons, and heavy ions of direct solar origin (e.g. from flares); and 3) a background of galactic cosmic rays ranging from several MeV to highly relativistic energies.  Knowledge of the near-Earth energetic particle environment is important in establishing the natural radiation hazard to humans at high altitudes and in space, as well as risk assessment and warning of episodes of surface charging, deep dielectric charging, and single event upset of satellite systems.  Energetic particle precipitation into Earth’s ionosphere also causes disturbance and disruption of radio communications and navigation systems.

The SEISS particle sensors shall include a magnetospheric particle sensor (MPS), a solar and galactic proton sensor (SGPS), and an energetic heavy ion sensor (EHIS).

The SEISS objectives are as follows:

- Provide data essential to NOAA’s Space Weather Operations and to the long-term record of changing conditions in the space environment.

- Maintain continuity with measurements provided in past and current Geostationary Operational Environmental Satellite (GOES) Series Spacecraft.

- Provide multiple measurements characterizing the charged particle population, including measurements of the electron, proton, and heavy ion fluxes.

- Be in Normal Operational Mode during on orbit storage, through eclipse, and spacecraft maneuvering.

## Document Overview

This document contains all performance requirements for the SEISS suite of instruments and Ground Support Equipment (GSE).  This document, the General Interface Requirements Document (GIRD), and the SEISS Unique Instrument Interface Document (UIID) define all instrument to spacecraft interfaces for the SEISS.

## Terminology

The term “(TBD)”, which means “to be determined”, applied to a missing requirement means that the instrument contractor determines the missing requirement.

The term “(TBR)”, which means “to be refined/reviewed”, means that the requirement is subject to review for appropriateness and subject to revision.  The contractor is liable for compliance with the requirement as if the “TBR” notation did not exist.  The “TBR” merely provides an indication that the value is more likely to change in a future modification than requirements not accompanied by a “TBR”.

## Definitions

Throughout this document, the following definitions apply:

Accuracy:  Refers to the error in a measurement, that is the difference between the measured and true value.  It includes both systematic and random errors.  Systematic errors must be estimated from an analysis of the experimental conditions and techniques.  Random errors can be determined, and reduced, through repeated measurements under identical conditions and a standard deviation calculated.  The magnitude of a random error shall be taken as three standard deviations (3σ).

All requirements/all performance requirements/ all operational requirements:  Refers to any performance characteristic or requirement in the GIRD, SEISS PORD, SEISS UIID.

Cadence:  The time interval between the start of successive data collection sequences.

Data Latency:  The time interval between the end of a data collection sequence and the time that the data is available at the spacecraft interface.

Eclipse:  Defined as when the solar disk is occulted by the Earth or Moon, as viewed from the spacecraft.

Flux:  The number of particles crossing a unit area from a unit solid angle in a unit time. The directional-differential flux is given in units: (cm2 s sr keV)-1 or (cm2 s sr MeV)-1 and the directional-integral flux is given in units: (cm2 s sr)-1.

Goal:  A requirement that is desirable to achieve.

Launch:  The period of time between lift off and the separation of the GOES-R series satellite from the launch vehicle.

Station keeping:  On-orbit spacecraft maneuver that corrects for orbital drifts.

Threshold: A requirement that must be met.

Transfer Orbit:  The sequence of events that transpires to establish the GOES-R series satellite on-station after the GOES-R series satellite has separated from the launch vehicle.

Unit:  A functional subdivision of a subsystem and generally a self-contained combination of items performing a function necessary for the subsystem’s operation.  Examples are electronics unit and sensor unit.

Yaw Flip:  An on-orbit maneuver that rotates the spacecraft 180º about the spacecraft z axis (yaw).  The net effect reverses the signs of the roll and pitch axes while maintaining yaw pointing at nadir.

## Requirement Applicability

All requirements apply over the entire life of the SEISS.

Data performance requirements in this SEISS PORD apply to data after all ground processing, except as indicated.

# Applicable Documents

Various parts of this requirements document refer to some of these documents.

Structural Design and Test Factors of Safety for Spaceflight Hardware, NASA, Document Number NASA-STD-5001, June 21, 1996.

General Specification for Assemblies, Moving Mechanical, for Space and Launch Vehicles, Document Number MIL-A83577B, February 1, 1988.

Space Mechanisms Handbook, Document Number NASA TP-1999-206988.

General Environmental Verification Specification for STS and ELV Payloads, Subsystems and Components, Document Number GSFC GEVS-SE, June 1, 1996.

Eastern and Western Range Policies and Procedures, Document Number EWR-127-1, October 23, 2000.

Standard General Requirements for Safe Design and Operation of Pressurized Missile and Space Systems, Document Number MIL-STD-1522, September 4, 1992.

# Sensor Requirements

## Sensor Definition

### SEISS Modes

The SEISS shall execute commands to individually enable and disable each autonomous function of the SEISS.

All SEISS instruments shall individually and independently accept commands.

The SEISS instruments shall provide operation mode telemetry at the same rate as the instrument science data.

The SEISS instruments shall initiate all commanded mode transitions in no more than 20 seconds after receipt of command.

The SEISS instruments shall provide limits and triggers of autonomous functions that are changeable by command.

The SEISS instruments shall transition from the current mode to any other mode without causing permanent damage to themselves.

The SEISS instruments shall provide command and housekeeping telemetry functions in all powered modes.

#### Safe Mode

Each SEISS instrument shall provide a Safe Mode.

The SEISS instruments shall provide a thermally and optically safe configuration for an indefinite period of time while in Safe Mode.

The SEISS instruments shall provide an autonomous command function to enter Safe Mode upon detection of instrument contractor defined internal faults capable of causing permanent damage to the instrument.

The SEISS instruments shall enter safe mode upon command.

The SEISS Instruments shall transition to Safe Mode, whether commanded or autonomous, in no more than 1 second.

The SEISS shall transition from Safe Mode to Normal Operational Mode in no more than 10 minutes.

#### Normal Operational Mode

All SEISS instruments shall provide a Normal Operational Mode.

#### Instrument Diagnostic Mode

Each SEISS instrument shall provide an Instrument Diagnostic Mode.

The SEISS shall perform the following functions while operating in the Instrument Diagnostic Mode.

- Download RAM contents.

- TBD

- Send dwell data (increased samples per second of a particular telemetry measurand).

### On-Orbit Operations

The SEISS shall operate normally, within specification, while flying aboard a 3-axis stabilized, geostationary spacecraft with orbital limit constraints as stated in the GIRD and UIID.

#### Reserved

#### Reserved

#### Eclipse

The SEISS shall  continuously operate without reduction in performance during eclipse periods.

#### Operations After Maneuvers

##### Yaw Flip

The SEISS shall continuously operate without reduction in performance during and after a yaw flip.

##### Stationkeeping

The SEISS shall continuously operate without reduction in performance while the spacecraft performs stationkeeping maneuvers.

#### Activation

The SGPS and EHIS shall be turned on within TBD minutes following launch.

The MPS shall be turned on within TBD minutes following launch.

The SEISS instruments shall meet all requirements within 30 minutes of SEISS turn on.

#### On-Orbit Storage

The SEISS shall continuously operate without reduction in performance during on orbit storage.

## Sensor Requirements

### General Requirements

The requirements in this section apply to all instruments of the SEISS.

#### Noise

For bands below 30 keV, the total instrument noise shall not exceed 10% of a band’s threshold energy.

For bands with threshold energies between 30 keV and 100 keV, the total instrument noise shall not widen the effective response by more than 10 keV.

For bands above 100 keV, total instrument noise shall not widen the effective response by more than 10% of a band’s threshold energy.

#### Stability

The SEISS shall provide individual electronic discriminator levels defining the energy band upper and lower edges that do not change by more than ±3% over the predicted operating conditions.

#### In-Flight Calibration

The SEISS instruments shall provide an in-flight calibration mode that verifies basic instrument operation and determines the value of the energy band edges.

The SEISS shall determine electronic discriminator levels with an accuracy of ±3%.

The SEISS in-flight calibration shall be both self-terminating and able to be terminated by ground command.

#### Ground Calibration

The instruments shall be fully characterized prior to delivery, including the measurement of the instrument response to in-band (including direction, energy, and species) and out-of-band particles.

The energy dependent and the directional responses of the instruments shall be determined for energies ranging from below the detector’s low-energy threshold to energies for which the particle flux is below the instrument detection threshold.

#### Out-of-Band Response

The SEISS shall limit the response to out-of-band particles (including direction, energy, and species), in any channel to no more than 10% of the response to in-band particles.

### MPS Requirements

#### Low Energy Electrons and Protons

##### Flux Measurement Range

The MPS shall provide low energy electron and proton flux measurements in the range 30 eV to 30 keV.

The MPS shall determine the proton and electron flux in 15 evenly spaced logarithmic energy bands per species.

##### Accuracy

The MPS shall provide a flux measurement accuracy of 25% (Goal 10%), determined through ground calibration.

##### Spatial Coverage and Field of View

The MPS shall provide at least five non-overlapping and equally spaced bins in the YZ plane.

The field of view shall be 170 degrees in the YZ plane, 30 degrees (TBR) in the XZ plane, and symmetric about the XZ and YZ planes.

The coordinate system is referenced to the spacecraft BRF axes defined in GIRD paragraph 3.1.4-2.

##### Data Rate

The MPS refresh rate shall be at least once per 30 seconds.

The MPS data latency shall be less than 5 seconds. (TBR)

##### Maximum and Minimum Flux

The MPS shall detect the minimum flux with a minimum of 10 counts above background in each energy channel for measurements taken over a 5 minute interval.

The MPS output shall not decrease as the flux increases up to three times the specified maximum flux.

a) Electrons

The MPS shall measure the electron flux according to the following energy spectra (E is the energy in keV):

Minimum flux:

0.03 – 30keV		Flux [cm-2 s-1 sr-1 keV-1] = 9. x 104 E-1.3

Maximum flux:

0.03 – 30keV		Flux [cm-2 s-1 sr-1 keV-1] = 1.5 x 109 E-1.3

b) Protons

Minimum flux:

0.03 – 30keV		Flux [cm-2 s-1 sr-1 keV-1] = 40. E-0.8

Maximum flux:

0.03 – 30keV		Flux [cm-2 s-1 sr-1 keV-1] = 1.1 x 107 E-0.8

#### Medium and high energy electrons and protons

##### Measurement Range

The MPS shall measure electron flux in the range of 30 keV to 4 MeV.

The MPS shall determine the electron flux in 10 evenly spaced logarithmic energy bands plus one integral channel for energies greater than 2 MeV.

The MPS shall measure proton flux in the range of 30 keV to 1 MeV.

The MPS shall determine the proton flux in 7 evenly spaced logarithmic energy bands.

##### Accuracy

The MPS shall provide a flux measurement accuracy of 25% (Goal 10%), determined through ground calibration.

##### Spatial Coverage and Field of View

The MPS shall provide at least five non-overlapping and equally spaced bins in the YZ plane.

The field of view shall be 170 degrees in the YZ plane, 30 degrees (TBR) in the XZ plane, and symmetric about the XZ and YZ planes.

The coordinate system is referenced to the spacecraft BRF axes defined in GIRD paragraph 3.1.4-2.

##### Data Rate

The refresh rate shall be at least once per 30 seconds.

The data latency shall be less than 5 seconds. (TBR)

##### Maximum and Minimum Flux

The MPS shall detect the minimum flux with a minimum of 10 counts above background in each energy channel for measurements taken over a 5 minute interval.

The MPS output shall not decrease as the flux increases up to three times the specified maximum flux.

a) Electrons

The MPS shall measure the electron flux according to the following energy spectra (E is the energy in keV):

Minimum flux:

30– 4,000 keV:		Flux [cm-2 s-1 sr-1 keV-1] = 1.2 x 107 E-2.8

Maximum flux:

30– 4,000 keV:		Flux [cm-2 s-1 sr-1 keV-1] = 2.3 x 1011 E-2.8

b) Protons

The MPS shall measure the proton flux according to the following energy spectra (E is the energy in keV):

Minimum flux:

30– 1,000 keV:	Flux [cm-2 s-1 sr-1 keV-1] = 8. x 102 E-1.8

Maximum flux:

30– 1,000 keV:	Flux [cm-2 s-1 sr-1 keV-1] = 5 x 107  E-1.3

### SGPS Requirements

#### Measurement Range

The SGPS shall provide proton flux measurements in the energy range from 1 MeV to 500 MeV.

As a threshold, the flux shall be determined in 10 evenly spaced logarithmic energy bands up to 500 MeV.

As a goal, the SGPS shall provide proton flux measurements >500 MeV.

As a goal, one integral channel shall be provided for flux measurements > 500 MeV.

#### Accuracy

The SGPS shall provide a flux measurement accuracy of 25% (Goal 10%), determined through ground calibration.

#### Spatial Coverage and Field of View

The SGPS shall consist of two identical sensor heads, each with a field of

view of 60 degrees in XY plane, 60 degrees in the XZ plane, and symmetric

about the XY and XZ planes, with the +X or the -X axis as the view

direction.

The coordinate system is referenced to the spacecraft BRF axes defined in GIRD paragraph 3.1.4-2.

#### Data Rate

The refresh rate shall be at least once per 1 minute.

The data latency shall be less than 5 seconds. (TBR)

#### Minimum and Maximum Flux

The SGPS shall resolve the largest likely solar particle event.  The spectrum for this event can be represented as (E is the energy in keV):

Minimum flux:

1,000 – 500,000 keV		Flux [cm-2 s-1 sr-1 keV-1] = 8. x 102 E-1.8

Maximum flux:

1,000 – 500,000 keV		Flux [cm-2 s-1 sr-1 keV-1] = 2. x 1012 E-2.8

The SGPS shall detect the minimum flux with a minimum of 10 counts above background in each energy channel for measurements taken over a 5 minute interval.

The SGPS output shall not decrease as the flux increases up to three times the specified maximum flux.

### EHIS Requirements

#### Measurement Range

The EHIS shall provide flux measurements in the energy range from 10 MeV/nucleon to 200 MeV/nucleon.

The EHIS shall detect and distinguish between the following mass groups: He, C-N-O, Ne-S, and the Fe group.

The flux within each mass group shall be determined in 5 evenly spaced logarithmic energy bands within the specified range.

#### Accuracy

The EHIS shall provide a flux measurement accuracy of 25% (Goal 10%), determined through ground calibration.

#### Spatial Coverage and Field of View

The EHIS shall have a conical field of view with a half angle of 30 degrees (TBR) about the minus Z axis of the spacecraft BRF specified in GIRD paragraph 3.1.4-2.

#### Data Rate

The refresh rate shall be at least once per 5 minutes.

The data latency shall be less than 5 seconds. (TBR)

#### Minimum and Maximum Flux

The EHIS shall measure the heavy ion abundances during the largest likely solar particle event.  The minimum and maximum fluxes within each of the four mass bands can be represented as (E is the energy in MeV):

Maximum Flux:	Flux [cm-2 s-1 sr-1 (MeV/nuc)-1] = 5 x 104  (E/nuc) -2.3

Threshold:

Minimum Flux:	Flux [cm-2 s-1 sr-1 (MeV/nuc)-1] = 1.1 x 10-2  (E/nuc) -1

Goal:

Minimum Flux:	Flux [cm-2 s-1 sr-1 (MeV/nuc)-1] = 2.7 x 10-3  (E/nuc) -1

The EHIS shall detect the minimum flux with a minimum of 10 counts above background in each energy channel for measurements taken over a 5 minute interval.

The EHIS output shall not decrease as the flux increases up to three times the maximum flux.

## Design Requirements

### Reliability

The SEISS shall have a Reliability (R) of at least 0.6 after 10 years of on-orbit operations, preceded by up to 5 years of ground storage and up to 5 years of operation during on-orbit storage.

The SEISS shall have a Mean Mission Duration (MMD) of 8.4 years for a design life of 10 years.

The SEISS units of any Flight Model shall be interchangeable, without modification, with the equivalent units of any other SEISS Flight Model.

The SEISS shall withstand without damage the sudden removal of operational power.

### Mechanical Requirements

Each SEISS unit structure shall possess sufficient strength, rigidity and other characteristics required to survive the critical loading conditions that exist within the envelope of handling and mission requirements.

#### Design Limit Loads

The structure shall be capable of withstanding all limit loads without loss of any required function.

Limit loads are defined as all worst case load conditions including temperature effects from the environments expected during all phases of the structure’s service life including manufacturing, ground handling, transportation, environmental testing, integration, pre-launch, launch and on-orbit operations and storage.

#### Non-Linear Loads

The SEISS structures shall be capable of withstanding redistribution of internal and external loads resulting from any non-linear effects including deflections under load.

#### Yield Strength

The SEISS structures shall be able to support yield loads without detrimental permanent deformation.  Yield loads are limit loads multiplied by the appropriate protoflight yield factor of safety specified in NASA-STD-5001.  For structural elements containing beryllium or beryllium alloys, the prototype yield factor of safety is 1.4.

While subjected to any operational load up to yield operational loads, the resulting deformation shall not interfere with the operation of the SEISS flight units.  Operational load is defined as the expected on-orbit loads while the SEISS is operating.

#### Ultimate Strength

The SEISS structures shall be able to support ultimate loads without fracture or collapse for at least 3 seconds including ultimate deflections and ultimate deformations of the flight unit structures and their boundaries.  However, when proof of strength is shown by dynamic tests simulating actual load conditions, the 3-second limit does not apply.  Ultimate loads are limit loads multiplied by the appropriate protoflight ultimate factor of safety specified in NASA-STD-5001.  For structural elements containing beryllium or beryllium alloys, the prototype ultimate factor of safety is 1.6.

#### Structural Stiffness

Stiffness of the SEISS unit structures and their attachments shall be designed by consideration of their performance requirements and their handling, transportation and launch environments.

Special stowage provisions shall be used if required to prevent excessive dynamic amplification during handling, transportation and transient flight events.

#### Unit Stiffness

The fundamental resonant frequency of each SEISS flight unit shall be 50 Hz or greater when the flight unit is constrained at its spacecraft interface.

#### Material Properties

Material properties shall be based on sufficient tests of the material meeting approved specifications to establish design values on a statistical basis.

Design values shall account for the probability of structural failures and loss of any required function due to material variability.

The instrument contractor shall specify the source and statistical basis of all material properties used in the design.

#### Critical Members Design Values

For critical members, design values shall be selected to assure strength with a minimum of 99 percent probability and 95 percent confidence.

Structural members are classified as critical when their failure would result in loss of structural integrity of the flight units.

#### Redundant Members Design Values

For redundant members, design values shall be selected to assure strength with a minimum of 90 percent probability and 95 percent confidence.

Structural members are classified as redundant when their failure would result in the redistribution of applied loads to other structural members without loss of structural integrity.

#### Selective Design Values

As an exception to Sections “Critical Members Design Values” and “Redundant Members Design Values”, greater design values may be used if a representative portion of the material used in the structural member is tested before use to determine that the actual strength properties of that particular structural member will equal or exceed those used in the design.

#### Structural Reliability

The strength, detailed design, and fabrication of the structure shall prevent any critical failure due to fatigue, corrosion, manufacturing defects and fracture throughout the life of the SEISS resulting in the loss of any mission objective.

Accounting for the presence of stress concentrations and the growth of undetectable flaws, the SEISS structures shall withstand loads equivalent to four complete service lifetimes.

While subjected to any flight operational load up to limit flight operational loads, the resulting deformation of the residual SEISS structures shall not interfere with the operation of the SEISS.

After any load up to limit loads, the resulting permanent deformation of the residual instrument flight unit structures shall not interfere with the operation of the SEISS.

#### Mechanisms

Deployment, sensor, pointing, drive, separation mechanisms and other moving mechanical assemblies may be designed using MIL-A-83577B and NASA TP-1999-206988.

All SEISS mechanisms shall meet performance requirements while operating in an earth gravity environment with any orientation of the gravity vector.

Moving mechanical assemblies shall have torque and force ratios per section 2.4.5.3 of GEVS-SE using a NASA approved classification of each instrument mechanism.

For all operating points of the actuators, all rotational actuators shall have available a continuous maximum torque output greater than 7.0 milli-Newton meters.

For all operating points of the actuators, all linear actuators shall have available a continuous maximum force output greater than 0.28 N.

For SEISS mechanisms using closed-loop control, gain and phase margins shall be greater than 12 dB, and greater than 40 degrees, respectively.   The margins shall include the effects of the dynamic properties of any flexible structure.

All SEISS mechanisms requiring restraint during launch shall be caged during launch without requiring power to maintain the caged condition.

All SEISS mechanisms requiring restraint shall be released from a caged condition by command.

All SEISS mechanisms requiring restraint shall be returned to a caged condition ready for launch by either command or by manual actuation of an accessible caging device.

#### Pressurized Units

SEISS pressurized systems shall follow the requirements in accordance with EWR-127-1 and MIL-STD-1522A for the design of pressurized systems.

The SEISS shall have no open fluid reservoirs when delivered to the spacecraft contractor.

#### Alignment Reference

The SEISS sensor units shall have fiduciary marks locating the X, Y, and Z axes of the units.

### Thermal Requirements

#### Temperature Limits

The SEISS contractor shall establish Mission Allowable Temperatures (MAT) for the SEISS with at least 5 K of analytical/test uncertainty.

Thermal margin is defined as the temperature delta between MAT versus the bounding predictions plus analytical uncertainty.

The SEISS shall maintain thermally independent units and their internal components within MAT limits during all flight operational conditions including bounding worst-case environments.

#### Non Operational Temperature

The Non-Operational Temperatures (NOT) range shall extend at least 20 K warmer than the hot MAT and at least 20 K colder than the cold MAT.

The cold Non-Operational Temperature shall be 248K or colder.

#### Thermal Control Hardware

There shall be two or more serial and independent controls for disabling any heater where any failed on condition would cause over-temperature conditions or exceed the instrument power budget.

The SEISS heaters shall be sized to have 25% margin for worst case conditions.

The SEISS survival heaters shall be thermostatically controlled.

### On-Board Processor Requirements

#### Flight Load Non-volatile Memory

The entire flight software image shall be contained in non-volatile memory at launch.

#### Commandable Reinitialization

The On-Board Processor shall provide for reset by command.

#### Deterministic Power-on Configuration

The On-Board Processor shall initialize upon power-up into a predetermined configuration.

#### Fail-safe Recovery Mode

The Instrument shall provide a failsafe recovery mode dependant on a minimal hardware configuration capable of accepting and processing a minimal command subset sufficient to load and dump memory.

### Flight Software Requirements

#### Language and Methodology

All software developed for the SEISS shall be developed with ANSI/ISO standard languages and a widely-accepted, industry-standard, formal software design methodology.  Minimal use of processor-specific assembly language is permitted for certain low-level programs such as interrupt service routines and device drivers with NASA approval.

#### Software Module Upload

The flight software shall be reprogrammable on-orbit without computer restart.

The flight software shall be capable of being uploaded in Computer Software Units (CSUs) and is usable immediately after completion of the modified unit upload.

Activation of the modified CSUs shall not require completion of an upload of the entire flight software image.

#### Flexibility and Ease of Software Modification

The SEISS flight software shall be deterministic in terms of scheduling and prioritization of critical processing tasks to ensure their timely completion.

All software data that are modifiable and examinable by ground operators shall be organized into tables that can be referenced by table number so table data can be loaded and dumped by the ground without reference to memory address.

The definition of instrument commands within the ground database shall not be dependent on physical memory addresses within the flight software.

#### Version Identifiers

All software and firmware versions shall be implemented with an internal identifier (embedded in the executive program) that can be included in the instrument engineering data.

This software identifier shall be keyed to the configuration management process.

#### Flight Processor Resource Sizing

During development, flight processors providing computing resources for instrument subsystems shall be sized for worst case utilization not to exceed the capacity shown below (measured as a percentage of total available resource capacity):

Flight Processor Resource Utilization Limits

|  | S/W PDR | S/W CDR | S/W AR |
| --- | --- | --- | --- |
| RAM Memory | 40% | 50% | 60% |
| ROM Memory | 50% | 60% | 70% |
| CPU | 40% | 50% | 60% |

#### Software Event Logging

The flight software shall include time-tagged event logging in telemetry.

The event messages shall include all anomalous events, mode transitions, and system performance events.

All flight software components shall utilize a common format for event messages.

The flight software shall provide a means for ground command to enable and disable queuing of individual event messages.

The flight software shall buffer a minimum of 1000 event messages while the event messages are queued for telemetering to the ground.

The event message queue shall be configurable by command to either  (a) discard the new events, or (b) overwrite oldest events when the queue is full.

The flight software shall maintain counters for:

- the total number of event messages generated

- the number of event messages discarded because of queue overflow

- the number of event messages not queued due to being disabled.

#### Warm Restart

The flight software shall provide a restart by command with preservation of the event message queue and memory tables.

#### Memory Tests

The flight software shall provide a mechanism to verify the contents of all memory areas.

#### Memory Dump

The flight software, and associated on-board computer hardware, shall provide the capability to dump any location and any size of on-board memory to the ground upon command.

The flight software memory dump capability shall not disturb normal operations and instrument data processing.

#### Telemetry

Telemetry points sampled by the instrument shall be controlled by an on-orbit modifiable table.

The sample rate of every instrument telemetry point shall be controlled by an on-orbit modifiable table.

### Power Requirements

#### Power Regulators and Supplies

The SEISS power regulators and supplies shall have a phase margin of greater than 35 degrees.

The SEISS power regulators supplies across the spacecraft shall have a gain margin of greater than 20 dB.

#### Fuses

The SEISS shall not contain fuses.

#### Test Connectors

The SEISS shall have flight qualified covers for all test point connectors.

### Magnetic Properties

The change in the magnetic field produced by the SEISS sensor, electronics, or power supply modules shall be less than 30 nanoTesla peak-to-peak for any operating mode, up to a single low pass bandwidth of 1.0 Hz, in any axis when measured at a distance of 1 meter from any face of a module.

### Spacecraft Level Ground Testing

The SEISS shall accommodate operational testing in all modes and states for indefinite periods during Spacecraft level Thermal Vacuum in at least the following two orientations:

  - Spacecraft +Y axis aligned with the gravity vector and pointed down.

  - Spacecraft –X axis aligned with the gravity vector and pointed down.

### Ground Support Equipment and Development Facilities

#### Electrical System Test Equipment

The Electrical System Test Equipment (ESTE) shall operate the SEISS and ground support equipment during performance verification and calibration testing.

The ESTE shall simulate the spacecraft interface with power, clock pulses, command, and telemetry functions.

The ESTE shall include all test equipment necessary to operate and control the SEISS in all phases of operation and test modes.

The ESTE shall generate and maintain command logs.

The ESTE shall limit check all health and safety data.

The ESTE shall capture and archive all raw SEISS data.

The ESTE shall provide near-real time and off line data analysis of all SEISS data necessary to determine the performance characteristics of the instrument.

The ESTE shall interface with the Spacecraft Ground Support Equipment at the Spacecraft Contractor’s facility to extract SEISS science and engineering data.

The ESTE shall prohibit hazardous or critical commands being sent to the SEISS without operator verification.

#### Flight Software Development Environment

The Flight Software Development Environment (FSDE) shall consist of the hardware and software systems used for realtime, closed loop testing on flight like hardware to develop, test, validate, and demonstrate the flight software is ready for Government acceptance.

The FSDE shall support all lifecycle activities (development, test, and validation) simultaneously.

The FSDE shall contain all items (software, databases, compilers, debuggers, etc.) needed to prepare flight software for the target processor.

The FSDE shall contain engineering (hardware) models of necessary flight hardware as well as dynamic software models comprising the remainder of the instrument and the necessary on-orbit environment.

#### Shipping Container

The SEISS shipping container shall be compatible with shipment by air or air-ride van.

The SEISS shipping container shall be climate controlled and purgable.

The SEISS shipping container shall have internal temperature, humidity, and pressure monitors with external indicators.

The SEISS shipping container shall have shock recorders.

The SEISS shipping container shall meet all contamination control requirements imposed on the SEISS instrument units.

The SEISS shipping container shall be painted white and stenciled to indicate NASA property, content, and structural certification.

The SEISS GSE shipping containers shall be compatible with shipment by air or air-ride van.

The SEISS GSE shipping containers shall be painted white and stenciled to indicate NASA property, content, and structural certification.

# Acronyms

| ACA | After Contract Award |
| --- | --- |
| AI | Action Item |
| AIR | Action Item Review |
| ANSI/ISO | American National Standards Institute / International Organization of Standards |
| AR | Acceptance Review |
| BRF | Body Reference Frame |
| CCP | Contamination Control Plan |
| CDR | Critical Design Review |
| CMP | Configuration Management Plan |
| CMS | Configuration Management System |
| CPU | Central Processing Unit |
| CSU | Computer Software Unit |
| dB | Decibel |
| DOORS | Dynamic Object-Oriented Requirements System |
| EHIS | Energetic Heavy Ion Sensor |
| ESD | Electro-Static Discharge |
| ESTE | Electrical System Test Equipment |
| FMEA | Failure Mode Effects Analysis |
| FMECA | Failure Mode Effects and Criticality Analysis |
| FMP | Financial Management Plan |
| FPCCR | Formulation Phase Concept and Cost Review |
| FSDE | Flight Software Development Environment |
| FTA | Fault Tree Analysis |
| GIRD | General Interface Requirements Document |
| GOES | Geostationary Operational Environmental Satellite |
| GSE | Ground Support Equipment |
| GSFC | Goddard Space Flight Center |
| Hz | Hertz |
| ICD | Interface Control Document |
| IV&V | Independent Verification and Validation |
| K | Kelvin |
| MAID | Master Action Item Database |
| MAR | Mission Assurance Requirements |
| MAT | Mission Allowable Temperature |
| MeV | Mega Electron Volts |
| MLI | Multilayer Insulation |
| MMD | Mean Mission Duration |
| MPS | Magnetospheric Particle Sensor |
| MRD | Mission Requirements Document |
| MTR | Midterm Review |
| N | Newton |
| NASA | National Aeronautics and Space Administration |
| NOAA | National Oceanic and Atmospheric Administration |
| NOT | Non-Operational Temperature |
| OBP | On-Board Processor |
| PDR | Preliminary Design Review |
| PMP | Project Management Plan |
| PORD | Performance and Operational Requirements Document |
| PR | Progress Review |
| PRA | Probabilistic Risk Assessment |
| R | Reliability |
| RA | Recommended Approach |
| RAM | Random Access Memory |
| RFA | Request for Action |
| RFI | Request for Information |
| RMP | Risk Management Plan |
| ROM | Read Only Memory |
| S/W | Software |
| SDP | Software Development Plan |
| SEISS | Space Environment In-Situ Suite |
| SEL | Single Event Latch-up |
| SEMP | Systems Engineering Management Plan |
| SEP | Systems Engineering Process |
| SEU | Single Event Upset |
| SGPS | Solar and Galactic Proton Sensor |
| SLOC | Software Lines of Code |
| SOW | Statement of Work |
| TBD | To Be Determined |
| TBR | To Be Reviewed |
| TRL | Technology Readiness Level |
| TS | Trade Study |
| UIID | Unique Instrument Interface Document |
| VP | Verification Plan |