POLAR Spacecraft Status As of: Tues, 29 Nov, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:56=AN STIP data only | NOAA-14J AM: 20:57=AN STIP data only | NOAA-15K AM: 17:57=AN GAC data only | NOAA-16L PM: 14:54=AN GAC&LAC data | NOAA-17M AM: 22:24=AN GAC&LAC data | NOAA-18N PM 13:54=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU-1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ Investigating instability | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate ROLL Rgmode=PASSIVE Gyro-1 Off 10/24/05 Gyro-3 Off 6/10/04 Gyro chans X-Z only TOAR 454 RGyro roll estimate gains updated 11/17 | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation Probable collision on 20 Nov at 10:31z | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Momentum shift transition started 1 Nov ended 18 Nov. |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase each orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/3/03) #2 has 3 chans inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B | SSRs 1,2,3,4,5 Safestate=5B Current spikes TOAR 450 |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 OFF OFF 13Nov-13Dec | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT 2 omni=rcp Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) | ArrayOff +60 since 6/23/05 Full Sun Sun Angle 15 up to 22 in early Jan Batts 1&2=LRC Batt 1&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -50 Batts 1&3V/T=6/9 Batt2 VT=7/9 Since 11/22/05 Eclipse all year Sun angle 49 Steady trend Batts 1-3= LRC Degraded shunts SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Up to 15 mid-Dec Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 41 Start new uptrend Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Erratic Frequent scan motor current surge Occasional imagery bar codes Channels 2&4 APT | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Variable No bar codes since 12 Oct. Status upgraded 10/18/05 TCE24 OFF 4/14/04 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal 7/12/05 FW mode=Hi Powr | Operational Imagery high levels radiometric noise TOAR 441 CLOSED Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | Operational Status downgraded to Yellow 15 Aug 05 LW channel 1-12 noise TOAR 448 LW Noise improved since 14 Oct |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 Investigating change in motor current trend |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU8 off TOAR 449 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 as of 27 Sept | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous TED shutdown 24 Sept | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Thermal downtrend ended 10 Oct | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	There were no changes to N12 during the past reporting period.

NOAA-14:	The N14 AVHRR scan motor continues to experience frequent current spikes that affect imagery primarily by causing

occasional bar codes on HRPT images.   Synch delta is also highly variable but does seem to benefit from the once per orbit rephase enable operation that is executed out of stored commands over the South Pole (illustration 1).

Power balance appears to have been optimized with the last solar array offset move (to -50 degrees from -45) and battery V/T alterations that occurred on 22 Nov.  Previous to these reconfigurations, the batteries were only reaching full charge with a 3-4 minute margin before entering darkness.  Furthermore, once the batteries did reach full charge, the resultant shunt load increase was so significant that bus voltage regulation appeared to be at risk.  Since the reconfiguration, the batteries reach full charge much earlier in the sunlit portion of the orbit while concurrently shunt load has been significantly reduced to the point that the bus voltage is once again within stable regulation (illustrations 2-5).  A “test” of the batteries capacity actually (albeit inadvertently) occurred on 28 Nov when during a call up pass a non HRPT STX transmitter was left on for an entire orbit.  Previous to the 22 Nov reconfiguration such a situation might have been cause for concern.  However, in this case, the battery voltage drawdown during eclipse remained well above previous maximum draw downs.  With the power balance optimized, a prerequisite for the proposed MSU end of life “tilt test”, explained in previous weekly reports, has been accomplished.  With this power configuration and all power related issues staying the same, the power subsystem is GO to support the tilt test if and when it is approved by NOAA management.   On the other hand, other than the serendipitous outcome of the most recent EPS reconfiguration, no further effort has gone into planning the MSU end of life “tilt test” on N14 that has been addressed in previous Weekly Reports.

NOAA-15:	N15 VTX-1 (APT data) remains off because of an RF conflict with N12 and will remain off until 13 Dec.  Otherwise, all N15 subsystems were nominal relative to recent performance during the past week.  One item of note was the AVHRR scan motor current which did surge approximately 8 mAmps on 28 Nov and has since stabilized within the same high low range values but also at this higher absolute level.  This situation has become something of a pattern for this AVHRR in recent months where the scan motor current quickly runs up then stabilizes at a new higher level and then a week or so later, just as abruptly falls an equal amount and stabilizes at the new lower level. These surges and drops are typically not accompanied by significant changes in component temperatures, synch delta or image quality.   See illustration 6 for a view of the N15 AVHRR behavior, illustrations 7 and 8 for HIRS and AMSU performance and illustration 9 for a depiction of N15’s ADACS subsystem.

NOAA-16:	The N16 AVHRR scan motor current was relatively stable and unchanged during the past week at near nominal values

that are exclusive of bar coded imagery and MIRP rephase frame losses.  However, the scan motor current value still remains within the threshold that wave patterns are still evident on extreme close-ups of HRPT images.  Thermally, the AVHRR components have also stabilized at their all time high values reached last week but still well below the threshold where TCE24 will have to be commanded back on.  Other N16 payloads were also nominal and stable during the past week (illustrations 10 and 11).

The N16 ADACS subsystem remained stable within improved values after the uploaded of updated Rgyro roll estimation filter gains on 17 Nov into the control CPU (only).  With the improvement of N16 roll rates and errors and Y-wheel motor currents and temperatures sustained over the past 11 days it is expected that this update is a success and will be made permanent by commanding it into the non-control CPU sometime this week.  Originally, the new gains were only installed on the control CPU in case of instability.  If the new gains had threatened attitude performance, a switch of control to the backup CPU (which still had the old gain values) would have maintained spacecraft attitude.  See illustration 12-14 for depictions of the sustained stability of N16 roll axis performance.

NOAA-17:	After experiencing and quickly recovering from an apparent collision with an as yet undetermined space object on 20

Nov, just about every N17 component value returned to its pre-collision equilibrium within 24-48 hours of the collision occurring. Two days following this event, EMOSS engineers generated over 500 plots encompassing all N17 subsystems and a very representative collection of component values and determined that no apparent permanent effect had occurred on any subsystem of this spacecraft because of this event.  This full system analysis was distributed as a power point document to a large number of engineers who were part of the Tiger Team investigating this event (and is available to anybody else upon request).    The Tiger Team convened on 22 Nov to try and determine the specific facts of the event with engineers from NOAA, EMOSS, NASA, Lockheed and Air Force Space Command in attendance.  The analysis and conclusions from this meeting were generally incorporated, along with additional EMOSS analysis, into an Event Report (SER-05-P467) which included over 20 plot attachments and was submitted by EMOSS to NOAA management on 28 Nov.  The text narrative of this report can be found on subsequent pages of this report.  Otherwise N17 was generally stable and nominal during the past week with some slight instabilities showing up in the AVHRR scan motor but nothing that has not been experienced on numerous previous occasions.  See illustrations 15 and 16 for payloads and illustrations 17 and 18 for ADACS analysis.  Refer to the full Event Report or the TOAR currently being generated by EMOSS engineers for a complete package of graphical depictions of the collision event.

NOAA-18:	In performing analysis on N18 NOAA engineers detected that the MHS Flywheel Drive Motor which rotates

in the opposite direction of the MHS scanner to counter the angular momentum of the scanner, has seen it motor current increase beginning on or about 3 Nov while the scanner motor has remained stable (illustration 19).  The MHS is presently in a thermal uptrend but no other value measuring amperage on the MHS is showing any distinct trends at this time.  EMOSS engineers are not sure of the implication of this increase but are watching it closely and coordinating with other MHS engineers to make that determination.   Otherwise N18 payload suite was nominal during the past week (illustration 20).

The N18 Pitch Torquer coils are once again performing unloading after going through a period of a couple of weeks where they were not needed as the Z-momentum on N18 transitioned from a negative value to a positive one while Reaction Wheel speed/direction went from positive values to negative ones.  This was reported on in the previous weekly report but the transition now appears to have completed and stabilized (illustration 21).

NOAA/EMOSS Event Report   SER-05-P467

(Narrative extracts)

On, November 20 at 11:02z the on-duty AET saw miscompares on the mnemonics BGYRXCON (X gyro consistency check failure), BRYCOIL (Roll-Yaw torquer coil switched to back-up), and BRYCSINH (autonomous Roll-Yaw coil switching inhibited).  In addition, BZMOMENT (z axis momentum) was flagging Red High and contacted engineering who arrived just before a Barrow call up pass at 12:47z.  The pass showed that the spacecraft momentum and wheel speeds were abnormally high, but nominal ADACS control mode was still selected.

Engineering began to assess the situation with the limited telemetry available.  The RY coil switch and the inhibiting of further switching were the expected Flight Software response to reaction wheel speeds that were too high after the end of a wheel unloading period.  The gyro inconsistency flag would be a good indicator of the time the anomaly started but would not convey much other information.

Four possible causes for the anomaly were identified:  1) a collision with a foreign object, 2) a gyro failure resulting in the reaction wheels being driven by faulty data, 3) a RY coil failure that added momentum, 4) a propellant leak that added momentum.  It was decided to enable thruster firing during the next pass if the RWA speeds looked too high.  Thrusters would be disabled at the end of the pass because of the possibility of a faulty gyro.  It was decided not to perform any other commanding until data from the 14:43z pass could be analyzed.

At a 14:43z pass it was clear that the spacecraft was still in nominal mode, that the coils were unloading the excess momentum

in the system, and that the spacecraft appeared to be healthy.  The dump data fixed the start of the anomaly at 10:31z at which point N17 was at location; 58.042 South latitude, 167.786 West longitude and 827.9289 Km altitude, south-east of New Zealand, moving toward the ascending node.  It was clear that a collision was the only one viable possibility.  Momentum jumped nearly simultaneously on all three axes, eliminating the possibility of an RY coil anomaly.  Propellant pressures showed no changes, which ruled out a leak.  Because the total momentum of the spacecraft had changed, a gyro anomaly could also be ruled out.

Commanding was prepared for the 16:23z Wallops pass to restore the RY coil to primary, to re-enable the autonomous coil switching, and to clear the gyro inconsistency flag.  The commands were sent with no problems.  The data at this pass and a call-up Barrow pass at 17:56z both showed telemetry consistent with expectations.

With the spacecraft recovered to a nominal configuration and the probable cause of the anomaly identified as a collision, telemetry data were analyzed for signs of damage that the collision may have caused.  No single event upsets were recorded on either CPU for the entire day.  The only abnormalities noted in the telemetry seemed to be temporary responses to the attitude anomaly, including an increase in RWA bearing temperatures.  Of particular concern was possible damage to the solar array, since the large area is subject to a high probability of impact.  No changes in solar array performance were discernable.

The attitude errors induced by this large event were corrected by the control system in about 13 minutes. The recovery took place without the need for thruster firings. There was no evidence of RCE leaks. The coil switching that took place was as per software design. The momentum imparted in the collision was off loaded in about two revs, although it took the rest of the day for the momentum profile to phase back to the normal cycle.

The largest error was in yaw with an excursion over 10 deg.  Yaw exhibited a classic underdamped control behavior, evidenced by a sawtooth pattern of yaw rate.  The yaw reaction wheel speed and the commanded torque in showed that the control torque was saturated for 3 cycles.  Yaw reaction wheel speed was actually non-linear for several seconds.  Roll and pitch error were much less (1 deg in roll and less than 0.2 in pitch).

Note that the momentum level telemetry (BXMOMENT, BYMOMENT, BZMOMENT) can be misleading. The axis momentum levels are calculated in the nitrogen gas unloading software as the sum of wheel and body angular momenta read from the gyros.   Weights are also applied to spacecraft body rates relative to reaction wheel momentum.  The scale factors are 1.25 for yaw rate and 1.2 for pitch and roll body rates.    Thus, to accurately measure the total external momentum imparted to the spacecraft by the event, the net change in reaction wheel speed was used.  Measurements of the wheel speeds were taken between the onset of the impulse and the point where the control system had damped out the error (approximately 13 minutes), and all the external momentum was stored in the wheels.  (Several minutes of magnetic coil torquing is neglected.)  Differencing the nominal wheel momentum accumulation profile over the same orbit angles from the previous orbit gives a net momentum change due to the event of (-77, +61, +20) in-lb-sec, and a total magnitude of 100.2 in-lb-sec.  The sign of the momentum change is consistent with the initial rate transients observed at the impulse.

Approximately 7 minutes after the impulse, the spacecraft entered the southern E/W unloading region and the momentum began to unload . This was the point where unload thresholds for yaw and roll RWA's were met. The unloading was insufficient at the end of this region, however, and the roll/yaw coil switched to backup because the X RWA speed was still too high. 

Although November 20 is near the end of the Leonid meteor shower timeframe, a Leonid impact is a clear possibility.  Sources (http://lists.meteorobs.org/pipermail/meteorobs/2005-November/003520.html) show indications of increased Leonid activity in

the hours before the impact.  To evaluate the likelihood of a Leonid event, the NOAA-17 orbit geometry was modeled using STK-VO.  The Leonid radiant was visible (not occulted) at the time of the impact.  Since the impulsive torque vector is dependent on location of the impact from the spacecraft center of mass and the orientation of the Force vector (velocity), there is a plenum of trajectories that could generate the observed disturbance.  However, the large component in roll/yaw suggest an impact on the solar array, which could occur either from the quadrant of the Leonid radiant (Leonid impact), or along the velocity vector (orbiting debris impact).  Because the solar array position was approximately 120 deg at the time of the anomaly, impact from either the anti-velocity or anti-Leonid vector would occur on the back (non-cell side) of the array.

To parameterize the mass of a possible impacting object very approximately, the total angular momentum exchange (100 in-lb-sec) may be resolved into linear momentum and related to an impulsive torque:

N = dL/dt

N dt = 100 in-lb-sec  = 11.3  Nm-sec

(R x F) dt  = 11.3  Nm-sec

[R x (M dV/dt)]dt  = 11.3  Nm-sec

M ~ 11.3 / (R dV)  kg

Varying effective moment arm between 1m (impact on the body) and 3m (impact on the array), and velocity between 10 km/sec (representative orbital debris relative velocity) and 70 km/sec (Leonid particle velocity) gives the following particle mass parameterization:

| Case | Moment Arm (R) | Relative Velocity (V) | Particle Mass |
| --- | --- | --- | --- |
| Orbiting debris; body impact | 1m | 10 km/sec | 1.1 gm |
| Orbiting debris; S/A impact | 3m | 10 km/sec | 375 mg |
| Leonid; body impact | 1m | 70 km/sec | 160 mg |
| Leonid; S/A impact | 3m | 70 km/sec | 54 mg |

Thus, the momentum exchange is consistent with impact of an orbiting debris mass of 1 gram (order of magnitude), or a Leonid particle in the 50-100 mg range (a 2-sigma Leonid particle size distribution).

HRPT 29 Nov at 14:00z

Illustration 1:  NOAA-14 AVHRR Health Analysis

(The large current spikes continue affecting the scan motor. At times the value is nominally within the 150 mAmps range.  It just hasn’t been able to stabilize there.  Imagery is sometimes bar coded and sometimes nominal.  It is probable that most nominal images are a result of the MIRP rephases enable operations that are conducted once per orbit over the South Pole rather than once per day as was previously the case.

Illustration 2:  NOAA-14 EPS Health Analysis

(The SA move and VT change on 22 Nov appears to have had the desired affect of increasing battery voltages while decreasing shunt workload and allowing better bus voltage regulation.)

Illustration 2:  N14 Power Analysis part 1

(The SA and VT change of 17 Nov appears to have not been effective at reducing shunt stress.  Depicted in this plot is the 12 hour period immediately following the VT change.)

Illustration 3:  N14 EPS Analysis (part 2)

(No problems in the battery thermal situation as a result of the VT change either.)

Before Array Move						            After Array Move

Illustration 4:  N14 Power Analysis (Part 3)

(Much improved, nominal and stable for the first time in many weeks.)

Illustration 5:  N14 Power Analysis Long Term Effects

(A year in the life of N14 power performance with reconfigurations depicting the effects on key power subsystem components.)

Illustration 6:  N15 AVHRR Analysis

(Scan motor current surging again but stabilized on JDAY 333.  Synch delta and thermal situation still look good imagery remains nominal.)

Illustration 7:  N15 HIRS Analysis

(Nominal and stable.)

Illustration 8:  N15 AMSU Analysis

(Like HIRS, nominal and stable)

ILLUSTRATION 9:  N15 ADACS Analysis

(Nominal and stable.  Appear to be entering the seasonal effect of larger Yaw increases which should continue for several weeks, as it does each year at this time.)

ILLUSTRATION 10:  N16 AVHRR Analysis

(About as nominal and stable as it has been in many months.)

ILLUSTRATION 11:  N16 AVHRR Imagery Analysis

(Minor wave patterns persist but otherwise generally nominal imagery.)

Illustration 12:  N16 HIRS Analysis

(Generally stable but filter motor current recently equaled an all time high. Something to watch.)

\

Illustration 13:  N16 ADACS Analysis (Part 1)

(No more saturation on the Y-Wheel motor current, everything maintained nicely since the filter gain updates of 21 Nov.)

Illustration 14:  N16 ADACS Health Analysis (Part 2)

(Again very stable since the new gain updates went into effect.)

Illustration 15:  N17 AMSU Health Analysis

(Nominal and stable, just like last week.)

Illustration 16:  N17 AVHRR Health Analysis

(Generally nominal and stable notwithstanding a little instability from the scan motor current several days ago.)

Illustration 17:  N17 ADACS Analysis

(Put in perspective, the collision of 20 Nov seems to have been little more than a bump in the road.  Nominal and stable all week.)

Illustration 18:  N17 ADACS Health Analysis (Part 2)

(Everything returned quickly back to normal and there appear to be no fuel leakage whatsoever.)

6 Month trends						2 Month History

Illustration 19:  N18 MHS Flywheel Motor Current Trend Change

(A distinct change to the flywheel current on 3 Nov.  MHS is presently in a thermal uptrend).

Illustration 20:  N18 Payload Motor Current Analysis

(Everything else looks nominal and stable.)

Illustration 21:  N18 ADACS Analysis

(Z-axis transition appears to be complete, Pitch coil once again being used.)

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING November 25, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 11/18 | -892 msec | +276 msec | -345 msec | +346 msec | +173 msec | +121 msec |
| SAT. 11/19 | N/A | +274 msec | -345 msec | +349 msec | +173 msec | +120 msec |
| SUN. 11/20 | -903 msec | +275 msec | -345 msec | +349 msec | +174 msec | +122 msec |
| MON. 11/21 | -906 msec | +282 msec | -346 msec | +350 msec | +174 msec | +124 msec |
| TUE. 11/22 | -906 msec | +281 msec | -348 msec | +349 msec | +176 msec | +128 msec |
| WED. 11/23 | -903 msec | +281 msec | -349 msec | +352 msec | +177 msec | +129 msec |
| THU. 11/24 | -906 msec | +281 msec | -350 msec | +351 msec | +179 msec | +130 msec |