UNCLASSIFIED

UNIVERSAL DOCUMENTATION SYSTEM

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PRD/PSP

UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552047                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1000                          TIME LAST CHANGED:  11:05:40

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     The John F. Kennedy Space Center (KSC) Shuttle

Launch and Landing (L&L) Program Requirements Document (PRD) consists

of five volumes:

VOLUME I - Shuttle

The L&L PRD - Volume I - Shuttle is prepared by KSC in accordance

with the National Aeronautics and Space Administration (NASA)

Headquarters Document NMI 8610.10 dated May 20, 1977.  Requirements

for the flight segment are documented in the flight PRD prepared by

the Johnson Space Center (JSC).

VOLUME II - Payloads

The Volume II - Payloads - Basic contains management information.

A listing of the assigned payload annexes, and support requirements

that are not mission peculiar relating to the Space Transportation

System (STS) Payloads.

Payloads Annex

Each payload assigned a JSC-Payload Integration Plan Number and a

KSC-Launch Site Support Plan Number will be assigned a unique L&L

PRD Annex Number.  Separate annexes for the payload-unique require-

ments permits individual preparation, publication, update, and use

regardless of the payload flight assignment.  Further, the Annex

revisions cycle can be different and independent from that of the

L&L PRD Volume I - Shuttle and Volume II - Payloads.  The total

payload requirements of a particular mission can be developed by

combining the annexes for the individual payloads.

VOLUME III - International Space Station Basic

The Volume III - International Space Station Basic is prepared by KSC

in accordance with NASA Management Instruction NMI 8610.10 to document

support for the ground processing of the Space Station in preparation

for launch in addition to identified requirements that are generic to

experimentors support.  The On-Orbit support requirements will be

documented in on orbit documentation.

================================================================================

PAGE NUMBER:     1

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552047

ITEM NUMBER:        K1

VOLUME III - Launch Package Annex

Each Launch Package assigned a Mission Integration Plan Number will

be assigned a unique L&L Volume III Annex Number to document the

mission-peculiar ground processing requirements.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552048                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2                            DATE LAST CHANGED:  03/06/03

SECTION:            1000                          TIME LAST CHANGED:  11:13:49

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Automated Support Requirements System

The Automated Support Requirements System (ASRS) is an Intercenter/

Agency Electronic Data Processing and Transmission System for the

Communication of Support Requirements/Support Responses between NASA

and DoD Center/Agencies for the Space Transportation System and

Payloads.

The electronic transmission feature of the system permits immediate

dissemination of requirements and support information to all users.

The database storage feature can provide display of this information

in user familiar formats.

The ASRS provides all the necessary information that must normally

pass between the user and all contributing agencies in order to

support a program, mission, or test.

The system is sufficiently flexible to be used by support agencies

without affecting the internal management of the individual agencies.

Database - The ASRS database is located in the KSC IBM SPDMS-II

Computer System located at the VAB.  The database consists of a

series of logically independent databases which include:

1)  Launch & Landing Database - Shuttle (LLS)

================================================================================

PAGE NUMBER:     2

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552048

ITEM NUMBER:        K2

2)  Launch & Landing Database - Payloads (LLP)

3)  Flight Database - Shuttle (FLS)

4)  Flight Database - Payloads (FLP)

5)  Space Station Launch & Landing (SSL)

6)  Space Station Flight (TBD)

7)  Space Station on Orbit (TBD)

Each individual database is managed by the appropriate Database

Manager (DBM) who has total responsibility for management of the

database.  Each database contains only the support requirements and

support responses associated with that operating element.  Each center

is represented by a Requirements/Response (R/R) Manager who is

responsible for support requirements and support commitments by their

center.

The ASRS provides users with various online inquiries to manipulate

data in the database and provide the user with various management

reports.  It permits the release of requirement/response reports.

The ASRS should reduce the need for distribution of hardcopies of

requirements documents.  Every center/organization may now

retrieve the requirements of interest and print/distribute them

at each center/organization.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552049                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3                            DATE LAST CHANGED:  03/10/03

SECTION:            1000                          TIME LAST CHANGED:  10:49:57

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Support Notice Request Procedure

(Requirement Change Procedure)

General

-------

Requirements may be modified, added or deleted via the following

================================================================================

PAGE NUMBER:     3

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552049

ITEM NUMBER:        K3

requirement(s) change procedure.  In a PRD and/or OR, this can

be accomplished in one of two ways:

a.  Routine Change

b.  Expedite Change

:--------------------:

: Requirement Change :

:--------------------:

:

----------------------------------------

:                                      :

:--------------------:                 :--------------------:

:      Routine       :                 :      Expedite      :

: Requirement Change :                 : Requirement Change :

:--------------------:                 :--------------------:

:                                       :

:--------: :--------:                   :--------: :--------:

:   PRD  : :   OR   :                   :   PRD  : :   OR   :

: Change : : Change :                   : Change : : Change :

:--------: :--------:                   :--------: :--------:

A request for a change is submitted to the KSC Requirements/Response

(R/R) Manager via the KSC Form 31-71 or the electronic mail system.

Using the electronic mail system, the request would normally arrive

from the requester's Support Requirements System (SRS) Manager to the

KSC R/R Manager at SPDMS-II ID CI11PA.  If the request is made locally

at KSC, this would be accomplished either by the electronic mailbox

or by submitting the KSC Form 31-71 to the KSC R/R Manager.  This

request will state whether it is a mission unique change (one time

only) or a permanent change.  If it is an expedite requirement change

it must include a support need date.  Upon approval from the LSSM and

the KSC R/R Manager, the requirement(s) will be entered into the

Payload Database.

When a change is made, the support commitment for the requirement(s)

is changed to NOACK.  Responsible agencies (suppliers) will then

respond to each requirement with a support commitment and a support

response via the electronic mailbox system or with a hardcopy in the

================================================================================

PAGE NUMBER:     4

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552049

ITEM NUMBER:        K3

mail. Responses are sent to the KSC R/R Manager at SPDMS-II ID CI11PA.

Routine Requirement Change vs. Expedite Requirement Change

----------------------------------------------------------

A routine requirement change should be submitted for changes occurring

prior to 30 days before the support is needed.

An expedite requirement change should be submitted for changes

occurring from 30 to 3 days (72 hours) before the support is needed.

For changes occurring during the 3 days (72 hours) prior to the

support need, support should be scheduled real-time through the

appropriate channels.  In addition, the requirements will be

submitted to the KSC R/R Manager for proper documentation.

PRD Requirement Change vs. OR Requirement Change

------------------------------------------------

A PRD and/or OR requirement change may be made individually but the

OR requirement change must already exist in the appropriate supporting

PRD or it must be added to the PRD at the same time at the OR

requirement change.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552050                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4                            DATE LAST CHANGED:  07/03/02

SECTION:            1000                          TIME LAST CHANGED:  08:06:20

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Authorized support commitments and responses for

KSC Launch and Landing Payloads Documents

General

-------

All support commitments must be accompanied by a response.

Normally these responses would be routed through the responsible

agencies Support Requirements System (SRS) Manager to KSC's

Requirement/Response (R/R) Manager at SPDMS-II ID CI11PA.  KSC

================================================================================

PAGE NUMBER:     5

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552050

ITEM NUMBER:        K4

responses may be sent either by electronic mail or by hardcopy

directly to the R/R Manager with a copy to the support require-

ments group.  The following support commitments and responses are

valid in the Automated Support Requirements System (ASRS).

Commitments     Responses

-----------     ---------

WILCO           N/A (The response of N/A may be used with a

(Will Commit)   commitment of WILCO because the requirement is ok

exactly as stated.)

NOWLCO          An explanation as to why the NOWLCO was given and

(No Wilco)      what action (if any) the requester must take to

remedy the problem.

NOCMT           Normally used when support cannot be met at

(No Commit)     present but may be available in the future if

requester takes some kind of action such as

submitting a form, an ESR, etc.  This action

should be explained in the response.

SEERSP          Support will be given in part or whole, but not

(See Response)  exactly as requested.  Should include an

explanation as to why.

INWORK          further coordination and documentation required

(In Work)       before applicable response can be given.  should

include an explanation and expected response date.

NOACK           No response is given here because the responsible

(No Acknowl-    agency has not responded to the requirement.

edgement)

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552051                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5                            DATE LAST CHANGED:  07/03/02

SECTION:            1000                          TIME LAST CHANGED:  08:06:20

================================================================================

PAGE NUMBER:     6

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1000 - ADMINISTRATIVE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552051

ITEM NUMBER:        K5

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Requester and Supplier Designators

The 'Requester" designator has been used in this annex to direct

attention to support requirements that have been identified to

the KSC Launch Site Support Engineer (LSSE) by organizations other

than NASA (e.g. Hughes identifies the Hughes Aircraft Company as

the requesting organization).

The "Supplier" designator has been used in this annex to identify

the organization providing support to the support agency (e.g.,

USA identifies United Space Alliance as the support organization).

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:     7

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1010A - APPROVAL AUTHORITY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552260                  REQUIREMENT STATUS: DELETED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/08/99

ITEM NUMBER:        K1

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    553211                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/08/99

INITIAL DATE:       09/07/99

ITEM NUMBER:        K2                            DATE LAST CHANGED:  07/03/02

SECTION:            1010A                         TIME LAST CHANGED:  08:06:30

REQUESTER:          KSC

TEST CODE:          N/A

1.  PRECEDENCE

RATING:         N/A

2.  PRIORITY:       N/A

3.  INITIATION DATE:N/A

4.  COMPLETION DATE:N/A

5.  SPONSORING

AGENCY:         NASA OSF

6.  BASIC CONTRACT

NUMBER:         N/A

7.  AUTHORITY

(REFERENCES):   N/A

8.  NOTES:          This issue contains the Program Support Plan to

the Program Requirements Document for Annex SAQ -

MPLM Payload.  It also contains the following

RSR(s)/LSR(s):

RSR SAQ-01  Dated 09/07/99

9.  APPROVAL

AND DATE:

R. Thornburg

Payloads ASRS Database Manager

Kennedy Space Center

10. APPROVAL

AND DATE:

11. APPROVAL

AND DATE:

12. APPROVAL

================================================================================

PAGE NUMBER:     8

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1010A - APPROVAL AUTHORITY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    553211

ITEM NUMBER:        K2

AND DATE:

13. APPROVAL

AND DATE:

14. APPROVAL

AND DATE:

15. APPROVAL

AND DATE:

16. APPROVAL

AND DATE:

17. APPROVAL

AND DATE:

18. APPROVAL

AND DATE:

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:     9

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1020 - DISTRIBUTION LIST

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552053                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1020                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:

MPLM Special Distribution

Kennedy Space Center

--------------------

721S-S270/M. Dahm

721S-S270/P. Lintereur

721S-S270/B. Wills

721S-S280/T. Hernandez

721S-S280/B. Jackson

721S-S280/M. Kinslow

721S-S280/E. Stavros

721S-S280/J. Traylor

UB-C/R. Hill

UB-C/F. Santoro

UB-C2/J. Pope

UB-C4/T. Willingham

UB-G6/T. Anderson

UB-G6/D. Olsen

UB-M/G. Chin

UB-M/T. Corey

TOTAL = 16

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    10

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1031 - INDEX

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

SECTION           TITLE

-------     ------------------------------------------------------------------

1000       ADMINISTRATIVE

1010A      APPROVAL AUTHORITY

1020       DISTRIBUTION LIST

1031       INDEX

1050       ABBREVIATIONS/ACRONYMS

1051       TEST CODE DEFINITION

1052       SPECIAL CODE DEFINITION

1060       KEY TECHNICAL PERSONNEL

1070       TECHNICAL REFERENCES

1110       EXPERIMENTS DESCRIPTION

1310       TEST VEHICLE SYSTEM DESCRIPTION

2200       TELEMETRY DATA

2400       TIMING

2413       VISUAL COUNTDOWN

2700       COMMUNICATION

2730       VOICE NETWORK TRANSMISSION

2734       VIDEO/DATA NETWORK TRANSMISSION

2740       INTERCOMMUNICATIONS SYSTEMS

2750       VOICE TERMINATIONS

2755       VIDEO/DATA TERMINATIONS

2756       VOICE RADIO TERMINATIONS

2760       COMMUNICATIONS RECORDINGS

2780       OTHER COMMUNICATIONS

2800       VIDEO

3020       REAL TIME DISPLAYS

3100       PHOTOGRAPHY

3440       OTHER TECHNICAL SUPPORT - TRAINING

5200       TRANSPORTATION

5300       SERVICES

5310       SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

5311       SERVICES - FIRE AND RESCUE

5314       SERVICES - SECURITY AND SAFETY

5320       SERVICES - UTILITIES (ELECTRIC, WATER, AND SANITATION)

5321       SERVICES - HANDLING, STORAGE, AND DISPOSAL

5330       SERVICES - PROCUREMENT, SHIPPING, RECEIVING,  AND STOCK CONTROL

5340       SERVICES - PROPELLANTS, GASES, AND CHEMICALS

5342       SERVICES - CHEMICAL CLEANING

5351       SERVICES - GROUND HANDLING EQUIPMENT

5370       SERVICES - AIR OPERATIONS

5380       SERVICES - PHYSICAL AND LIFE SCIENCE EXPERIMENTS

================================================================================

PAGE NUMBER:    11

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1031 - INDEX

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:

ITEM NUMBER:        N/A

5410       LABORATORY - CHEMICAL AND PHYSICAL ANALYSIS

5420       LABORATORY - SPECIAL ENVIRONMENT

5430       LABORATORY - CALIBRATION

5440       LABORATORY - TECHNICAL SHOPS AND LABS

5600       FACILITIES

6000       OTHER SUPPORT

================================================================================

PAGE NUMBER:    12

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1050 - ABBREVIATIONS/ACRONYMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552261                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1050                          TIME LAST CHANGED:  13:02:53

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Abbreviations and Acronyms

The following Abbreviations and Acronyms are used in this document:

AAC       Aft Access Closure

AF        Active Flight

ALTEC     ASI Logistics and Technological Engineering Centre

ASI       Agenzia Spaziale Italiana

ASRS      Automated Support Requirements System

C&DH      Command and Data Handling

C&T       Communications and Tracking

CAPPS     Checkout, Assembly and Payload Processing Services

CBM       Common Berthing Mechanism

CCTV      Closed Circuit Television

CDSC      Communications Distribution and Switching Center

CELA      Cargo Element Lifting Assembly

CEWS      Cargo Element Work Stand

CITE      Cargo Integration Test Equipment

CSOC      Consolidated Space Operations Contract

DBM       Database Manager

DBR       Database Record

ECLSS     Environmental Control and Life Support System

ELSA      Emergency Life Support Apparatus

ERS       Element Rotation Stand

ESD       Electrostatic Discharge

GMT       Greenwich Mean Time

GSE       Ground Support Equipment

I/F       Interface

IDS       Integrated Daily Schedule

INT       Integrated Test

================================================================================

PAGE NUMBER:    13

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1050 - ABBREVIATIONS/ACRONYMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552261

ITEM NUMBER:        K1

IPR       Interim Problem Report

IRIG-B    Inter-range Instrumentation Group - B

ISS       International Space Station

IVT       Interface Verification Test

JSC       Johnson Space Center

KBPS      Kilo Bits Per Second

L&L       Launch and Landing

LC-39     Launch Complex - 39

LCC       Launch Control Center

LCD       Launch Countdown

LPIS      Launch Package Integration Stand

LSSE      Launch Site Support Engineer

LWF       Lightweight Floor

MATE      MPLM Applications Test Equipment

MBPS      Mega Bit Per Second

MCCH      Mission Control Center - Houston

MGSE      MPLM Ground Support Equipment

MLI       Multi-Layer Insulation

MPLM      Multi-Purpose Logistics Module

MSFC      George C. Marshall Space Flight Center

MSV       MPLM Support Vehicle

NASA      National Aeronautics and Space Administration

NASCOM    NASA Communication

NISN      NASA Integrated Services Network

NMI       NASA Management Instruction

NPRD      Network Program Requirements Document

OIS-D     Operational Intercommunication System - Digital

OMI       Operations and Maintenance Instruction

OPF       Orbiter Processing Facility

OR/OD     Operations Requirements/Operations Directive

OSR       Operations Support Room

OTC       Orbiter Test Conductor

OTV       Operational Television

================================================================================

PAGE NUMBER:    14

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1050 - ABBREVIATIONS/ACRONYMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552261

ITEM NUMBER:        K1

OSVS      Orbiter Space Vision System

P/L       Payload

PAF       Personnel Access Floor

PCR       Payload Changeout Room

PDV       Post Delivery Verification

PF        Passive Flight

PICO      Pre-Installation Checkout

PIP       Premium Internet Protocol

PLM       Payload Management

PMN       Program Model Number

PRD       Program Requirements Document

PRIT      Post Rack Installation Test

PSCN      Program Support Communications Network

PTCR      PAD Terminal Connection Room

PTD       Payload Test Director

QMR       Quality Monitor Room

R&R       Resupply and Return

R/F       Refrigerator/Freezer

RA        Requesting Agency

RID       Rack Insertion Device

RPA       Record and Playback Area

RSR       Routine Support Request

RTC       R&R Test Conductor

SA        Supporting Agency

SLF       Shuttle Landing Facility

SSPF      Space Station Processing Facility

TCDT      Terminal Countdown Test

TCMS      Test Control and Monitoring System

Tx/Rx     Transmitter / Receiver

UDS       Universal Documentation System

UF        Utilization Flight

UHF       Ultra High Frequency

ULF       Utilization / Logistics Flight

================================================================================

PAGE NUMBER:    15

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1050 - ABBREVIATIONS/ACRONYMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552261

ITEM NUMBER:        K1

VAB       Vehicle Assembly Building

VRSS      Video Relay Switcher System

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    16

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1051 - TEST CODE DEFINITION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552054                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1051                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Test Code Designators - The test codes used in

this PRD will identify the program requirements by location/

activity/mission phase.

Test

Code       Definition

------     ----------

AAC-HT     Aft Access Closure - Heater Test.

DAP        Dry Air Purge.

DFRC       Dryden Flight Research Center.

IVT        Interface Verification Test.

LCD        Launch Countdown.

MSV        Support requirements for activities involving the MPLM

Support Vehicle.

N/A        Not Applicable.

OPF        Support requirements for activities occurring at the OPF.

PAD        Support requirements for activities occurring at the PAD.

PICO       Pre-Installation Checkout.

POSTL      Post-landing activities to include OPF (early module

access) and SSPF activities.

PRIT       Post Rack Installation Test.

SLF        Shuttle Landing Facility support.

================================================================================

PAGE NUMBER:    17

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1051 - TEST CODE DEFINITION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552054

ITEM NUMBER:        K1

SSPF       Space Station Processing Facility.

TCDT       Terminal Countdown Test.

TRANS      Transportation of MPLM/GSE and associated support equipment.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    18

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1052 - SPECIAL CODE DEFINITION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552055                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1052                          TIME LAST CHANGED:  11:07:40

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Item Number

The entry "8. Item No.:" Appears on the first line of each requirement

and is followed by letters and numbers.  The Item No. provides a means

of identifying the requesting agency(s), sequence number and the

supporting agency(s).  Example  K3K:

K                    3                    K

(Requesting Agency)         (Number)       (Supporting Agency)

The standard-letter designators used for either requesting or

supporting agencies are listed in Document 501-79 Volume 2, Table

2-1.  The most commonly used designators are:

B - Lewis Research Center (LeRC)

D - Department of Defense (DoD)

E - 45th Space Wing (45th SPW)

G - Goddard Space Flight Center (GSFC)

H - Marshall Space Flight Center (MSFC)

I - Langley Research Center (LaRC)

J - Jet Propulsion Laboratory (JPL)

K - Kennedy Space Center (KSC)

T - Johnson Space Center (JSC)

X - Dryden Flight Research Facility (DFRF)

Y - NASA Headquarters (NASA)

Z - White Sands Test Facility (WSTF)

Primary support designators assigned are:  KSC (K) for Launch and

Landing support at KSC, GSFC (G) for network communication and

tracking support; ESMC (E) is designated as the primary DoD Point-

of-Contact (DoD Lead Range) for receipt of all range-oriented support

requirements and for coordination between all DoD ranges and DDMS for

all non-range DoD support not provided by Space Division.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    19

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552056                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Debra Caldwell

2.  ORGANIZATION:   NASA/TA-B2-E

3.  TITLE/OFFICE:   Networks and Communications Section

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-1547

6.  FACSIMILE:      (321) 867-3269

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552057                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Eve Stavros

2.  ORGANIZATION:   G122/721S-S280

3.  TITLE/OFFICE:   Launch Site Support Engineer (LSSE)

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P. O. Box 21233

Kennedy Space Center, FL  32815

5.  TELEPHONE NO.:  (321) 867-5791

6.  FACSIMILE:      (321) 867-6550

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552058                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Mark Sorensen

2.  ORGANIZATION:   N100/721S-S280

================================================================================

PAGE NUMBER:    20

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552058

ITEM NUMBER:        K3

3.  TITLE/OFFICE:   CAPPS R&R Manager

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P. O. Box 21233

Kennedy Space Center, FL  32815

5.  TELEPHONE NO.:  (321) 867-6101

6.  FACSIMILE:      (321) 867-6550

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552059                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Robert Hill

2.  ORGANIZATION:   NASA/UB-C

3.  TITLE/OFFICE:   NASA R&R IPT Lead

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-6049

6.  FACSIMILE:      (321) 867-6533

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552060                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Craig Catizone

2.  ORGANIZATION:   CSOC-601

3.  TITLE/OFFICE:   Communications and Data Analysis Systems

4.  BUSINESS ADDR:  Consolidated Space Operations Contract

Kennedy Space Center, FL  32815

5.  TELEPHONE NO.:  (321) 867-7722

6.  FACSIMILE:      (321) 867-3269

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    21

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552061                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Sharon Leek

2.  ORGANIZATION:   CSOC-601

3.  TITLE/OFFICE:   Communications and Data Analysis Systems

4.  BUSINESS ADDR:  Consolidated Space Operations Contract

Lockheed Martin

Kennedy Space Center, FL  32815

5.  TELEPHONE NO.:  (321) 867-7034

6.  FACSIMILE:      (321) 867-3269

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552062                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K7                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           James Pope

2.  ORGANIZATION:   NASA/UB-C2

3.  TITLE/OFFICE:   NASA Mission Integration Engineer

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-6169

6.  FACSIMILE:      (321) 867-0775

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552063                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K8                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:02:52

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Tomas Hernandez

================================================================================

PAGE NUMBER:    22

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552063

ITEM NUMBER:        K8

2.  ORGANIZATION:   G110/721S-S270

3.  TITLE/OFFICE:   Boeing Integration Engineer

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P. O. Box 21233

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-5459

6.  FACSIMILE:      (321) 867-6550

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570706                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K9                            DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Bud Jackson

2.  ORGANIZATION:   G122/721S-S280

3.  TITLE/OFFICE:   Boeing Mission Engineer

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P. O. Box 21233

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-5173

6.  FACSIMILE:      (321) 867-6650

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570707                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K10                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Emmett Crooks

2.  ORGANIZATION:   NASA/MSFC RO/SK-PL

3.  TITLE/OFFICE:   Marshall Resident Office

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-2198

================================================================================

PAGE NUMBER:    23

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570707

ITEM NUMBER:        K10

6.  FACSIMILE:      (321) 867-7108

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570708                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K11                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Ken Koby

2.  ORGANIZATION:   N150/721S-S270

3.  TITLE/OFFICE:   Boeing Mechanical Engineer (MPLM)

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P.O. Box 21233

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-5758

6.  FACSIMILE:      (321) 867-6550

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570709                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K12                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Mike Dahm

2.  ORGANIZATION:   N120/721S-S270

3.  TITLE/OFFICE:   Boeing Electrical Engineer

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P.O. Box 21233

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-5132

6.  FACSIMILE:

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    24

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    570710                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K13                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Jeff Traylor

2.  ORGANIZATION:   G122/721S-S280

3.  TITLE/OFFICE:   Boeing Payload Manager

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P.O. Box 21233

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-5393

6.  FACSIMILE:      (321) 867-6550

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570781                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K14                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Sylvia Segura

2.  ORGANIZATION:   LM/CSOC-109

3.  TITLE/OFFICE:   Voice Systems Requirements Engineer

4.  BUSINESS ADDR:  Consolidated Space Operations Contract

Lockheed Martin

Kennedy Space Center, FL  32815

5.  TELEPHONE NO.:  (321) 867-2158

6.  FACSIMILE:      (321) 867-3320

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570960                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K15                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

================================================================================

PAGE NUMBER:    25

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570960

ITEM NUMBER:        K15

1.  NAME:           Tracy Anderson

2.  ORGANIZATION:   NASA/UB-G6

3.  TITLE/OFFICE:   NASA Technical Integration Engineer

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-6142

6.  FACSIMILE:      (321) 867-6111

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570961                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K16                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Francesco Santoro

2.  ORGANIZATION:   NASA/UB-C

3.  TITLE/OFFICE:   Alenia/ASI Resident Office

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-6342

6.  FACSIMILE:      (321) 867-6613

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570962                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K17                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Bill Wills

2.  ORGANIZATION:   N100/721S-S270

3.  TITLE/OFFICE:   Manager - R&R Assembly and Integration

4.  BUSINESS ADDR:  The Boeing Company - Florida Operations

P. O. Box 21233

Kennedy Space Center, FL  32815

5.  TELEPHONE NO.:  (321) 867-5770

================================================================================

PAGE NUMBER:    26

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1060 - KEY TECHNICAL PERSONNEL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570962

ITEM NUMBER:        K17

6.  FACSIMILE:      (321) 867-5575

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570963                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K18                           DATE LAST CHANGED:  03/06/03

SECTION:            1060                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  NAME:           Dave Olsen

2.  ORGANIZATION:   NASA/UB-G6

3.  TITLE/OFFICE:   NASA Technical Integration Engineer

4.  BUSINESS ADDR:  National Aeronautics and Space Administration

Kennedy Space Center, FL  32899

5.  TELEPHONE NO.:  (321) 867-5924

6.  FACSIMILE:      (321) 867-0760

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    27

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1070 - TECHNICAL REFERENCES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    570712                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1070                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  REFERENCE;

A. ITEM:           K1

B. SECTION:        1110

2.  TITLE:          Payload Integration Plan (PIP) - International

Space Station Multi-Purpose Logistics Module,

NSTS - 21499

3.  PUBLISHER/DATE:

4.  SOURCE:

5.  SEC CL:

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    28

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1110 - EXPERIMENTS DESCRIPTION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    570711                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K1                            DATE LAST CHANGED:  03/06/03

SECTION:            1110                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     The Multi-Purpose Logistic Module (MPLM) is a

pressurized logistics module designed to supply and return cargo

requiring a pressurized storage environment to and from the

International Space Station (ISS) via the National Space

Transportation System (NSTS).  The MPLM is manifested Aft in the

Payload Bay with the MPLM Berthing Mechanism facing forward and is

designed to carry U.S. Lab System Racks, Resupply Storage Racks,

Experiment Racks, and Resupply Stowage Platforms (RSP's).

The MPLM will support two mission types, Active Flights (AF's) and

Passive Flights (PF's).

During Passive Flights and Active Flights the MPLM requires resources

both from the NSTS and from the ISS.  The terms 'active' and 'passive'

refer to cargo characteristics:  during any mission phase of passive

flights the cargo requires no power, data and cooling resources (dry

cargo), while during active flights the Refrigerator/Freezer (R/F)

racks require MPLM resources (cold cargo) in terms of power, data and

cooling capabilities.  In Passive Flights the NSTS resources are

needed for heaters power supply, the ISS resources for module

illumination, heating, atmosphere control etc.

Active Flights (AF's) are Utilization Flights (UF's) and (Utilization/

Logistics Flights (ULF's):  the MPLM will carry up to 16 racks, out of

which up to 5 are active racks.  It will return to earth with mission

dependent download mass.

Passive Flights (PFs) will mainly support the ISS outfitting.  The

MPLM will carry up to 16 passive racks to be transferred to the ISS

and it may return to earth with a different number of racks, or no

rack at all (typical outfitting mission).

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    29

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 1310 - TEST VEHICLE SYSTEM DESCRIPTION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552064                  REQUIREMENT STATUS: DELETED  R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

ITEM NUMBER:        K1

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    30

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2200 - TELEMETRY DATA

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552065                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2200                          TIME LAST CHANGED:  13:13:00

REQUESTER:          KSC

TEST CODE:          IVT             PAD

1. DESCRIPTION:     Provide the capability to record Orbiter

Telemetry Data (128 kbps).

Reference: Section 2755, Item K3K, DBR # 552077.

Section 2755, Item K4K, DBR # 552826.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (CSOC-601)

RESPONDER: SHARON LEEK

SUBSUPPLIER COMMITMENT: INFO                             RESPONSE DATE: 03/06/03

SUBSUPPLIER: USK-617

RESPONDER: RICK GLAZIER

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    31

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2400 - TIMING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552089                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2400                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide existing IRIG-B timing to the test stand

(Footprints 1 & 3) in the SSPF.  (Note: Existing)

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSR-4620

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Requires 48 hour notification.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552090                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            2400                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide an additional outlet of IRIG-B timing at

the test stand (Footprint 1) in the SSPF in support of the MPLM

Application Test Equipment (MATE).

Reference: Annex SAD, K2K for installation.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSR-4620

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Requires 48 hour notification.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    32

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2413 - VISUAL COUNTDOWN

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552814                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2413                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          PAD             SSPF

1. INFO TO BE

DISPLAYED:      GMT, Countdown

2. OPER PER FROM;

A. MIN.:

B. SEC.:

3. OPER PER TO;

A. MIN.:

B. SEC.:

4. OPER PER TOTAL;

A. MIN.:

B. SEC.:

5. INDICATORS;

A. QTY.:

B. MTG.:

6. LOC VIS INDTRS;

A. STA.:

B. BLDG.:          SSPF, OPF, PAD

C. RM.:            I-bay, Highbay, User Rooms (2387, 2397, and

2392, 2393), Bay 1, Pads A & B

D. LOC.:

7. REMARKS:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSR-4620

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    33

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2700 - COMMUNICATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552066                  REQUIREMENT STATUS: DELETED  R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

ITEM NUMBER:        K1K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    571083                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K1.1K                         DATE LAST CHANGED:  03/13/03

SECTION:            2700                          TIME LAST CHANGED:  15:29:14

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PICO            PRIT

SSPF

1. DESCRIPTION:     Provide ten (10) Industrial Area OIS channels for

use during SSPF testing of the MPLM in Footprint 1 as follows:

Ref.     Channel   Title

----------------------------------------------

1.1.1      117     OIS Control (Comm Problem)

1.1.2      010     R&R Test Conductor

1.1.3      011     INT (Integrated Test)

1.1.4      012     Lead C&DH / Power

1.1.5      013     Lead ECLSS

1.1.6      014     MPLM Ops

1.1.7      015     TCMS Ops

1.1.8      016     Alenia Offline Coord

1.1.9      017     Development Center Ops

1.1.10     018     IPR Troubleshooting

Note:  Channel 117 is used to report Comm problems.  If unit is not

working, call 867-4141.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    34

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2700 - COMMUNICATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    571084                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K1.2K                         DATE LAST CHANGED:  03/13/03

SECTION:            2700                          TIME LAST CHANGED:  15:29:34

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide ten (10) Industrial Area OIS channels for

use during SSPF integrated activities of the MPLM in Footprint 2

(LPIS) as follows:

Ref.     Channel   Title

----------------------------------------------

1.2.1      117     OIS Control (Comm Problem)

1.2.2      020     R&R Test Conductor

1.2.3      021     INT (Integrated Test)

1.2.4      022     Lead C&DH / Power

1.2.5      023     Lead ECLSS

1.2.6      024     MPLM Ops

1.2.7      025     TCMS Ops

1.2.8      026     Alenia Offline Coord

1.2.9      027     Development Center Ops

1.2.10     028     IPR Troubleshooting

Note:  Channel 117 is used to report Comm problems.  If unit is not

working, call 867-4141.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    571085                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K1.3K                         DATE LAST CHANGED:  03/13/03

SECTION:            2700                          TIME LAST CHANGED:  15:29:48

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PICO            PRIT

================================================================================

PAGE NUMBER:    35

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2700 - COMMUNICATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    571085

ITEM NUMBER:        K1.3K

SSPF

1. DESCRIPTION:     Provide ten (10) Industrial Area OIS channels for

use during SSPF testing of the MPLM in Footprint 3 as follows:

Ref.     Channel   Title

----------------------------------------------

1.3.1      117     OIS Control (Comm Problem)

1.3.2      030     R&R Test Conductor

1.3.3      031     INT (Integrated Test)

1.3.4      032     Lead C&DH / Power

1.3.5      033     Lead ECLSS

1.3.6      034     MPLM Ops

1.3.7      035     TCMS Ops

1.3.8      036     Alenia Offline Coord

1.3.9      037     Development Center Ops

1.3.10     038     IPR Troubleshooting

Note:  Channel 117 is used to report Comm problems.  If unit is not

working, call 867-4141.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552811                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/10/03

SECTION:            2700                          TIME LAST CHANGED:  09:56:39

REQUESTER:          KSC

TEST CODE:          OPF             PAD             POSTL

1. DESCRIPTION:     Provide fifteen (15) LC-39 Area OIS channels for

use during PAD testing and OPF post-landing activities of the MPLM

as follows:

================================================================================

PAGE NUMBER:    36

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2700 - COMMUNICATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552811

ITEM NUMBER:        K2K

Ref.      Channel    Title

--------------------------------------------------------------

2.1.1      117       OIS Control (Comm Problems)

2.1.2      133       PTD (P/L Test Director/ P/L Management 3)

2.1.3      134       RTC (R&R Payload Test Conductor)

2.1.4      138       JYVO (LC-39 Video Comm)

2.1.5      144       INT (Integrated Test)

2.1.6      154       INT (Integrated Test - Backup)

2.1.7      161       PE-1 (Shuttle Project Engineer)

2.1.8      164       P/L 1

2.1.9      174       MPLM Ops

2.1.10     184       P/L 3

2.1.11     233       Quality

2.1.12     234       PLM 1 (Payload Management 1)

2.1.13     244       PLM 2 (Payload Management 2)

2.1.14     254       P/L 4 (Payload 4)

2.1.15     264       ASI/Alenia (Altec Coord)

Note:  Channel 117 is used to report Comm problems.  If unit is not

working, call 867-4141.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552812                  REQUIREMENT STATUS: DELETED  R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

ITEM NUMBER:        K3K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552067                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            2700                          TIME LAST CHANGED:  13:03:26

================================================================================

PAGE NUMBER:    37

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2700 - COMMUNICATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552067

ITEM NUMBER:        K4K

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide 25 OIS-D headsets for personnel use in

the SSPF during MPLM testing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552068                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            2700                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          OPF             PAD

1. DESCRIPTION:     Provide 15 OIS-D headsets for personnel use in

MPLM pad and deintegration processing activities.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Headsets to be provided from Boeing Headset Pool.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    560009                  REQUIREMENT STATUS: DELETED  R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

ITEM NUMBER:        K6K

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    38

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2730 - VOICE NETWORK TRANSMISSION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552069                  REQUIREMENT STATUS: DELETED  R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

ITEM NUMBER:        K1G

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552819                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2G                           DATE LAST CHANGED:  03/13/03

SECTION:            2730                          TIME LAST CHANGED:  15:42:51

REQUESTER:          KSC

TEST CODE:          LCD             PAD

1.  STATIONS;

A. FROM:          KSC/CDSC

B. TO:            JSC via NISN

Channel  M/T  Assignment

-------  ---  ----------------

2.  CIRCUIT DESCR.: KSC LC-39 Area OIS  144     T   RTC

3.  CIRCUIT DESCR.: KSC LC-39 Area OIS  234     T   P/L Management 1

4.  CIRCUIT DESCR.: KSC LC-39 Area OIS  154     T   INT (Integrated

Test)

5.  CIRCUIT DESCR.: KSC LC-39 Area OIS  264     T   ASI/Alenia

6.  CIRCUIT DESCR.:

7.  CIRCUIT DESCR.:

8.  CIRCUIT DESCR.:

9.  CIRCUIT DESCR.:

10. CIRCUIT DESCR.:

11. CIRCUIT DESCR.:

12. CIRCUIT DESCR.:

13. CIRCUIT DESCR.:

14. CIRCUIT DESCR.:

15. CIRCUIT DESCR.:

16. TOTAL CIRCUITS: Four (4)

17. REFERENCE;

A. SECTION NO.:   2750

B. ITEM NO.:      K4KT, DBR # 570742

18. REMARKS:

SUPPLIER: GSFC       ORG: GSFC/450        (GODDARD SPACE FLIGHT CENTER       )

RESPONDER: TONY WILLIAMS

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:    39

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2730 - VOICE NETWORK TRANSMISSION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552819

ITEM NUMBER:        K2G

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570713                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K3G                           DATE LAST CHANGED:  03/06/03

SECTION:            2730                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PICO            PRIT

SSPF

1.  STATIONS;

A. FROM:          KSC/CDSC

B. TO:            JSC

Channel   M/T   Assignment

-------   ---   ----------

2.  CIRCUIT DESCR.: KSC Industrial Area OIS   010      T    RTC

3.  CIRCUIT DESCR.: KSC Industrial Area OIS   011      T    Integ Test

4.  CIRCUIT DESCR.: KSC Industrial Area OIS   012      T    Lead C&DH

5.  CIRCUIT DESCR.: KSC Industrial Area OIS   016      T    Alenia Ops

6.  CIRCUIT DESCR.:

7.  CIRCUIT DESCR.:

8.  CIRCUIT DESCR.:

9.  CIRCUIT DESCR.:

10. CIRCUIT DESCR.:

11. CIRCUIT DESCR.:

12. CIRCUIT DESCR.:

13. CIRCUIT DESCR.:

14. CIRCUIT DESCR.:

15. CIRCUIT DESCR.:

16. TOTAL CIRCUITS: Four (4)

17. REFERENCE;

A. SECTION NO.:   2750

B. ITEM NO.:      K1KT, DBR # 552072

18. REMARKS:        Required to provide Tx/Rx capability on SSPF

Highbay Footprint #1 OIS-D channels to ASI/ALTEC

personnel in Italy via JSC during TCMS testing at

KSC.

SUPPLIER: GSFC       ORG: GSFC/451        (GODDARD SPACE FLIGHT CENTER       )

================================================================================

PAGE NUMBER:    40

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2730 - VOICE NETWORK TRANSMISSION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570713

ITEM NUMBER:        K3G

RESPONDER: TONY WILLIAMS

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570714                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K4G                           DATE LAST CHANGED:  03/06/03

SECTION:            2730                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PICO            PRIT

SSPF

1.  STATIONS;

A. FROM:          KSC/CDSC

B. TO:            JSC

Channel  M/T  Assignment

-------  ---  ----------

2.  CIRCUIT DESCR.: KSC Industrial Area OIS   030     T   RTC

3.  CIRCUIT DESCR.: KSC Industrial Area OIS   031     T   Integ. Test

4.  CIRCUIT DESCR.: KSC Industrial Area OIS   032     T   Lead C&DH

5.  CIRCUIT DESCR.: KSC Industrial Area OIS   036     T   Alenia Ops

6.  CIRCUIT DESCR.:

7.  CIRCUIT DESCR.:

8.  CIRCUIT DESCR.:

9.  CIRCUIT DESCR.:

10. CIRCUIT DESCR.:

11. CIRCUIT DESCR.:

12. CIRCUIT DESCR.:

13. CIRCUIT DESCR.:

14. CIRCUIT DESCR.:

15. CIRCUIT DESCR.:

16. TOTAL CIRCUITS: Four (4)

17. REFERENCE;

A. SECTION NO.:   2750

B. ITEM NO.:      K2KT, DBR # 570740

18. REMARKS:        Required to provide Tx/Rx capability on SSPF

Highbay Footprint #3 OIS-D channels to ASI/ALTEC

================================================================================

PAGE NUMBER:    41

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2730 - VOICE NETWORK TRANSMISSION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570714

ITEM NUMBER:        K4G

personnel in Italy via JSC during TCMS testing at

KSC.

SUPPLIER: GSFC       ORG: GSFC/451        (GODDARD SPACE FLIGHT CENTER       )

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    42

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2734 - VIDEO/DATA NETWORK TRANSMISSION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    561051                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       10/26/01

ITEM NUMBER:        K1G                           DATE LAST CHANGED:  03/06/03

SECTION:            2734                          TIME LAST CHANGED:  13:53:31

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PAD             PICO

POSTL           PRIT            SSPF

1.  STATIONS;

A. FROM:          KSC PSCN Building (M6-39)

B. TO:            ASI Node, JSC Building 30

2.  CIRCUIT DESCR.: 1.544 Mbps Premium Internet Protocol (PIP)

circuit.

3.  CIRCUIT DESCR.:

4.  CIRCUIT DESCR.:

5.  CIRCUIT DESCR.:

6.  CIRCUIT DESCR.:

7.  CIRCUIT DESCR.:

8.  CIRCUIT DESCR.:

9.  CIRCUIT DESCR.:

10. CIRCUIT DESCR.:

11. CIRCUIT DESCR.:

12. CIRCUIT DESCR.:

13. CIRCUIT DESCR.:

14. CIRCUIT DESCR.:

15. CIRCUIT DESCR.:

16. TOTAL CIRCUITS: One (1)

17. REFERENCE;

A. SECTION NO.:   2755

B. ITEM NO.:      K6K

18. REMARKS:        To send video and data to ASI/ALTEC personnel in

Italy via JSC during TCMS testing at KSC per NPRD

2736.11.01 and 2736.11.02.  Technical Contact:

Bob Wilson, MSFC, 256-961-9391.

SUPPLIER: GSFC       ORG: GSFC/451        (GODDARD SPACE FLIGHT CENTER       )

SUBSUPPLIER:        (CSOC-601)

RESPONDER: TONY WILLIAMS

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    43

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2740 - INTERCOMMUNICATIONS SYSTEMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552071                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2740                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide four (4) portable OIS-D end instruments at

SSPF Footprint 1/3 element rotation stand with 100 feet of cable

for use for the MPLM integrated verification test and in support

of subsequent MPLM testing in the SSPF, to be scheduled in IDS 72

hours prior to required use.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570715                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/10/03

SECTION:            2740                          TIME LAST CHANGED:  09:56:54

REQUESTER:          KSC

TEST CODE:          OPF             POSTL

1. DESCRIPTION:     OIS End Instruments for MSV Interface (OPF Bay 1)

Ref    Location                      Type    Station

---    --------                      ----    --------

2.1    OPF Bay 1 - MSV I/F Panel      P       125-11

2.2    OPF Bay 1 - MSV I/F Panel      P       126-51

2.3    OPF Bay 1 - MSV I/F Panel      P       127-11

Note: Reference Section 2750, Item K8KT, DBR # 570720.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

================================================================================

PAGE NUMBER:    44

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2740 - INTERCOMMUNICATIONS SYSTEMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570715

ITEM NUMBER:        K2K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570716                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/10/03

SECTION:            2740                          TIME LAST CHANGED:  09:57:05

REQUESTER:          KSC

TEST CODE:          OPF             POSTL

1. DESCRIPTION:     OIS End Instruments for MSV Interface (OPF Bay 2)

Ref    Location                      Type    Station

---    --------                      ----    --------

3.1    OPF Bay 2 - MSV I/F Panel      P       124-11

3.2    OPF Bay 2 - MSV I/F Panel      P       126-11

3.3    OPF Bay 2 - MSV I/F Panel      P       127-51

Note: Reference Section 2750, Item K8KT, DBR # 570720.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570717                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/10/03

SECTION:            2740                          TIME LAST CHANGED:  09:57:16

REQUESTER:          KSC

TEST CODE:          OPF             POSTL

1. DESCRIPTION:     OIS End Instruments for MSV Interface (OPF Bay 3)

Ref    Location                      Type    Station

---    --------                      ----    --------

================================================================================

PAGE NUMBER:    45

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2740 - INTERCOMMUNICATIONS SYSTEMS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570717

ITEM NUMBER:        K4K

4.1    OPF Bay 3 - MSV I/F Panel      P       138-73

4.2    OPF Bay 3 - MSV I/F Panel      P       139-51

4.3    OPF Bay 3 - MSV I/F Panel      P       139-72

Note: Reference Section 2750, Item K8KT, DBR # 570720.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    46

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552072                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1KT                          DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  09:57:29

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PICO            PRIT

SSPF

1. DESCRIPTION:     MPLM Industrial Area Footprint 1 OIS Ground

Communications for TCMS testing activities (Aft Access Closure

Heater Test, Dry Air Purge, Pre-installation Checkout, and Post

Rack Installation Test).

:0:0:0:0:0:0:0:0:0:

Extensions/                      :1:1:1:1:1:1:1:1:1:

Ref.    Note    Terminations                     :0:1:2:3:4:5:6:7:8:

--------------------------------------------------------------------

1.1           RESPONSIBLE AGENCY:  KSC

1.1.1           CDSC for Recording               :R:R:R:R:R:R:R:R:R:

1.1.2     1     CDSC for Ext to JSC via NISN     :T:T:T: : : :T: : :

1.1.3           SSPF High Bay Footprint No. 1    :T:T:T:T:T:T:T:T:T:

1.1.4           SSPF Room 2251 (Video Switcher)  :T:T:T:T:T:T:T:T:T:

1.1.5           SSPF Room 2377 TCMS (Control/    :T:T:T:T:T:T:T:T:T:

User Room 5)

1.1.6           SSPF Room 2383 (Control/User     :T:T:T:T:T:T:T:T:T:

Room No. 4)

1.1.7           SSPF Room 2398 (QMR)             :T:T:T:T:T:T:T:T:T:

1.1.8           O&C Room 4289/4298               :T:T:T:T:T:T:T:T:T:

1.2           RESPONSIBLE AGENCY:  JSC

1.2.1     1     JSC for MCCH Dist                :T:T:T: : : :T: : :

Note 1: For extension to ASI/ALTEC in Italy.

Reference:  Section 2730, Item K3G, DBR # 570713.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

================================================================================

PAGE NUMBER:    47

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552072

ITEM NUMBER:        K1KT

SUPPLIER: JSC        ORG: JSC/DV          (JOHNSON SPACE CENTER              )

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570740                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K2KT                          DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  09:57:43

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PICO            PRIT

SSPF

1. DESCRIPTION:     MPLM Industrial Area Footprint 3 OIS Ground

Communications for TCMS testing activities (Aft Access Closure

Heater Test, Dry Air Purge, Pre-installation Checkout, and Post

Rack Installation Test).

:0:0:0:0:0:0:0:0:0:

Extensions/                      :3:3:3:3:3:3:3:3:3:

Ref.    Note    Terminations                     :0:1:2:3:4:5:6:7:8:

--------------------------------------------------------------------

2.1           RESPONSIBLE AGENCY:  KSC

2.1.1           CDSC for Recording               :R:R:R:R:R:R:R:R:R:

2.1.2     1     CDSC for Ext to JSC via NISN     :T:T:T: : : :T: : :

2.1.3           SSPF High Bay Footprint No. 3    :T:T:T:T:T:T:T:T:T:

2.1.4           SSPF Room 2251 (Video Switcher)  :T:T:T:T:T:T:T:T:T:

2.1.5           SSPF Room 2377 TCMS (Control/    :T:T:T:T:T:T:T:T:T:

User Room 5)

2.1.6           SSPF Room 2383 (Control/User     :T:T:T:T:T:T:T:T:T:

Room No. 4)

2.1.7           SSPF Room 2398 (QMR)             :T:T:T:T:T:T:T:T:T:

2.1.8           O&C Room 4289/4298               :T:T:T:T:T:T:T:T:T:

2.2           RESPONSIBLE AGENCY:  JSC

2.2.1     1     JSC for MCCH Dist                :T:T:T: : : :T: : :

================================================================================

PAGE NUMBER:    48

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570740

ITEM NUMBER:        K2KT

Note 1: For extension to ASI/ALTEC in Italy.

Reference:  Section 2730, Item K4G, DBR # 570714.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

SUPPLIER: JSC        ORG: JSC/DV          (JOHNSON SPACE CENTER              )

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552073                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  09:57:54

REQUESTER:          KSC

TEST CODE:          IVT             PAD

1. DESCRIPTION:     MPLM LC-39 Area OIS Ground Communications for IVT

:1:1:1:1:1:1:1:1:2:

Extensions/                      :3:3:3:3:4:5:6:7:3:

Ref.   Note    Terminations                     :2:3:4:8:4:4:1:4:2:

-------------------------------------------------------------------

3.1          RESPONSIBLE AGENCY:  KSC

3.1.1          CDSC for Recording               :R:R:R:R:R:R:R:R:R:

3.1.2          Firing Room P/L Consoles         :T:T:T:T:T:T:T:T:T:

AC-5, AC-6

3.1.3          PCR/PTCR                         :T:T:T:T:T:T:T:T:T:

3.1.4          Pad Base                         :T:T:T:T:T:T:T:T:T:

3.1.5          Pad White Room                   :T:T:T:T:T:T:T:T:T:

3.1.6          Pad P/L Trailers                 :T:T:T:T:T:T:T:T:T:

3.1.7          SSPF Room 2251 (Video Switcher)  :T:T:T:T:T:T:T:T:T:

================================================================================

PAGE NUMBER:    49

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552073

ITEM NUMBER:        K3K

3.1.8          SSPF Room 2377 (User Room #5)    :T:T:T:T:T:T:T:T:T:

3.1.9          SSPF Room 2383 (User Room #4)    :T:T:T:T:T:T:T:T:T:

3.1.10         SSPF Room 2392 (RPA)             :T:T:T:T:T:T:T:T:T:

3.1.11         SSPF Room 2397 (Control Rm #1)   :T:T:T:T:T:T:T:T:T:

3.1.12         O&C Room 4289/4298               :T:T:T:T:T:T:T:T:T:

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552074                  REQUIREMENT STATUS: DELETED  R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

ITEM NUMBER:        K3K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570742                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K4KT                          DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  09:58:15

REQUESTER:          KSC

TEST CODE:          LCD             PAD             TCDT

1. DESCRIPTION:     LC-39 Area Firing Rm 1 OIS Ground Communications -

Terminal Countdown Test (TCDT) and Launch Countdown (LCD).

:1:1:1:1:1:1:1:1:1:2:2:2:2:2:

Extensions/                :3:3:3:4:5:6:6:7:8:3:3:4:5:6:

Ref.   Note   Terminations               :3:4:8:4:4:1:4:4:4:3:4:4:4:4:

-----------------------------------------------------------------------

4.1          RESPONSIBLE AGENCY:  KSC

4.1.1          CDSC for Recording        :R:R:R:R:R:R:R:R:R:R:R:R:R:R:

4.1.2   1      CDSC for Ext to JSC via   : : : :T:T: : : : : :T: : :T:

NISN

4.1.3          LCC F/R 1 P/L Consoles    :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

4.1.4          LCC F/R 2 0234 & 0243     :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

================================================================================

PAGE NUMBER:    50

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570742

ITEM NUMBER:        K4KT

Consoles

4.1.5          LCC F/R 3 OSR Consoles    :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

4.1.6          PAD White Room            :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

4.1.7          O&C Room 4289/4298        :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

4.2          RESPONSIBLE AGENCY:  JSC

4.2.1   1      JSC for MCCH Dist         : : : :T:T: : : : : :T: : :T:

Note 1: Distribution to JSC for LCD only, for extension to ASI/ALTEC

in Italy.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: (CSOC-601)

RESPONDER: SHARON LEEK

SUBSUPPLIER COMMITMENT: INFO                             RESPONSE DATE: 03/06/03

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

SUPPLIER: JSC        ORG: JSC/DV          (JOHNSON SPACE CENTER              )

RESPONDER: KITTY CUNNINGHAM

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570743                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K5KT                          DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  10:00:05

REQUESTER:          KSC

TEST CODE:          LCD             PAD             TCDT

1. DESCRIPTION:     LC-39 Area Firing Rm 3 OIS Ground Communications -

Terminal Countdown Test (TCDT) and Launch Countdown (LCD).

================================================================================

PAGE NUMBER:    51

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570743

ITEM NUMBER:        K5KT

:1:1:1:1:1:1:1:1:1:2:2:2:2:2:

Extensions/                 :3:3:3:4:5:6:6:7:8:3:3:4:5:6:

Ref.  Note   Terminations                :3:4:8:4:4:1:4:4:4:3:4:4:4:4:

----------------------------------------------------------------------

5.1        RESPONSIBLE AGENCY:  KSC

5.1.1        CDSC for Recording          :R:R:R:R:R:R:R:R:R:R:R:R:R:R:

5.1.2   1    CDSC for Ext to JSC via     : : : :T:T: : : : : :T: : :T:

NISN

5.1.3        LCC F/R 3 P/L Consoles      :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

5.1.4        LCC F/R 2 0234 & 0243       :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

Consoles

5.1.5        LCC F/R 1 OSR Consoles      :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

5.1.6        PAD White Room              :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

5.1.7        O&C Room 4289/4298          :T:T:T:T:T:T:T:T:T:T:T:T:T:T:

5.2        RESPONSIBLE AGENCY:  JSC

5.2.1   1    JSC for MCCH Dist           : : : :T:T: : : : : :T: : :T:

Note 1: Distribution to JSC for LCD only, for extension to ASI/ALTEC

in Italy.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: (CSOC-601)

RESPONDER: SHARON LEEK

SUBSUPPLIER COMMITMENT: INFO                             RESPONSE DATE: 03/06/03

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

SUPPLIER: JSC        ORG: JSC/DV          (JOHNSON SPACE CENTER              )

RESPONDER: KITTY CUNNINGHAM

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:    52

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570743

ITEM NUMBER:        K5KT

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570741                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  10:00:19

REQUESTER:          KSC

TEST CODE:          PAD

1. DESCRIPTION:     LC-39 Area OIS Ground Communications - MPLM

Closeouts.

:1:1:2:

Extensions/                     :3:4:3:

Ref.    Note    Terminations                    :2:4:2:

-------------------------------------------------------

6.1           RESPONSIBLE AGENCY:  KSC

6.1.1           CDSC for Recording              :R:R:R:

6.1.2           F/R P/L Consoles AC-5, AC-6     :T:T:T:

6.1.3           PCR                             :T:T:T:

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: (CSOC-601)

RESPONDER: SHARON LEEK

SUBSUPPLIER COMMITMENT: INFO                             RESPONSE DATE: 03/06/03

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570721                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  10:00:33

REQUESTER:          KSC

================================================================================

PAGE NUMBER:    53

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570721

ITEM NUMBER:        K7K

TEST CODE:          MSV             POSTL           SLF

1. DESCRIPTION:     MPLM/MSV runway tow post-landing operations

:5:6:

Extensions/                   :0:0:

Ref.    Note    Terminations                  :0:0:

---------------------------------------------------

7.1           Responsible Agency:  KSC

7.1.1           CDSC for Recording            :R:R:

7.1.2           OPF Highbay Y-Ops desk        :T:T:

7.1.3           SSPF User Room 4              :T:T:

7.1.4           SSPF User Room 5              :T:T:

7.1.5           LCC P/L Consoles, AC-5, AC-6  :T:T:

7.1.6           LCC F/R OSR Consoles          :T:T:

500 Radio Net

600 Radio Net

Notes:  For communication with MSV operations via UHF radio.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570720                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K8KT                          DATE LAST CHANGED:  03/10/03

SECTION:            2750                          TIME LAST CHANGED:  10:00:48

REQUESTER:          KSC

TEST CODE:          MSV             OPF             POSTL

1. DESCRIPTION:     MPLM/MSV OPF Bay Post-Landing Operations

:1:1:1:1:1:1:2:2:5:6:

================================================================================

PAGE NUMBER:    54

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2750 - VOICE TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570720

ITEM NUMBER:        K8KT

Extensions/                   :3:3:3:3:4:5:3:6:0:0:

Ref.    Note    Terminations                  :2:4:5:8:4:4:2:4:0:0:

-------------------------------------------------------------------

8.1      1    Responsible Agency:  KSC

8.1.1           To CDSC for Recording         :R:R:R:R:R:R:R:R:R:R:

8.1.2   1,2     CDSC for EXT to JSC via NISN  : : : : :T:T: :T: : :

8.1.3           OPF MSV I/F Panel             :T:T:T:T:T:T:T:T:T:T:

8.1.4           OPF Highbay levels 11 & 13    :T:T:T:T:T:T:T:T:T:T:

8.1.5           LCC F/R P/L Consoles, AC-5,   :T:T:T:T:T:T:T:T:T:T:

AC-6

8.1.6           SSPF Rm 2383 (U/R #4)         :T:T:T:T:T:T:T:T:T:T:

8.1.7           SSPF Rm 2377 (TCMS U/R #5)    :T:T:T:T:T:T:T:T:T:T:

8.1.8           SSPF Rm 2398 (QMR)            :T:T:T:T:T:T:T:T:T:T:

8.1.9           O&C Room 4289/4298            :T:T:T:T:T:T:T:T:T:T:

8.2           Responsible Agency:  JSC

8.2.1   1,2     JSC for MCC Dist              : : : : :T:T: :T: : :

Note:

1. Support for MSV post-landing activities begins at R-8 hours.

2. Distribution to JSC for active MPLM missions only, for extension

to ASI/ALTEC in Italy.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

SUPPLIER: JSC        ORG: JSC/DV          (JOHNSON SPACE CENTER              )

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    55

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552075                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          PAD

1. DESCRIPTION:     VRSS/LC-39 OTV Connectivity (2 Required)

A. TYPE SERV.: OTV Transmission from the PCR

B. FROM:       LCC

C. TO:         O&C Building Room 4289 (VRSS)

D. REMARKS:    Required for extension of LC-39 OTV to the O&C during

MPLM PAD testing.

Reference: Section 2800, Item K5K, DBR # 552088.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552076                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          PAD

1. DESCRIPTION:     VRSS/SSPF OTV Connectivity (2 Required)

A. TYPE SERV.: OTV Transmission from the PCR

B. FROM:       O&C Room 4289 (VRSS)

C. TO:         SSPF Video Switch

D. REMARKS:    Required for extension of LC-39 OTV to the SSPF during

MPLM PAD testing.

Reference: Section 2800, Item K5K, DBR # 552088.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:    56

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552076

ITEM NUMBER:        K2K

SUBSUPPLIER: CSOC-601

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552077                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:14:49

REQUESTER:          KSC

TEST CODE:          IVT             PAD

1. DESCRIPTION:     Orbiter Telemetry Data

A. TYPE SERV.: One Digital Data Circuit, 128 kbps, Bi-Phase

B. FROM:       LCC

C. TO:         SSPF Room 2392 (RPA)

D. REMARKS:    Required for recording during MPLM PAD testing.

Reference Section 2200, Item K1K, DBR # 552065

for recording requirements.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

RESPONDER: DON GARCEAU

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552826                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          IVT             PAD

1. DESCRIPTION:     Digital Data Circuit

================================================================================

PAGE NUMBER:    57

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552826

ITEM NUMBER:        K4K

A. TYPE SERV.: Digital Data Circuit, 128 kbps, Bi-Phase

B. FROM:       SSPF Room 2392 (RPA)

C. TO:         SSPF Room 2397 (Control Rm #1)

D. REMARKS:    Required during PAD testing.  Data to be stripped to

14.4 kbps for viewing in 2397.

Reference: Section 2200, Item K1K, DBR # 552065

for recording requirements.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: USK-617

RESPONDER: RICK GLAZIER

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    561052                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       10/26/01

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PAD             PICO

POSTL           PRIT            SSPF

1. DESCRIPTION:     Ethernet Connectivity

A. TYPE SERV: Ethernet connectivity

B. FROM:      TCMS display server in SSPF 2377 (User Room 5)

C. TO:        ASI Rack in SSPF room 2377 (User Room 5)

D. REMARKS:   To send TCMS display data to ASI/ALTEC personnel in

Italy via JSC during TCMS testing at KSC.

Reference: Section 2755, Item K6K, DBR # 561056.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N110

RESPONDER: JEFF LEVITT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:    58

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    561052

ITEM NUMBER:        K5K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    561056                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       10/26/01

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PAD             PICO

POSTL           PRIT            SSPF

1. DESCRIPTION:     T-1 Circuit

A. TYPE SERV: T-1 circuit.

B. FROM:      ASI rack in SSPF 2377 (User Room 5).

C. TO:        PIP Router Interface, PSCN Building (M6-39).

D. REMARKS:   To send video and data to ASI/ALTEC personnel in Italy

via JSC during TCMS testing at KSC.

Reference: Section 2734, Item K1G, DBR # 561051

Section 2755, Item K5K, DBR # 561052

Section 2800, Item K3K, DBR # 561057

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N110

RESPONDER: JEFF LEVITT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570744                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:14:59

REQUESTER:          KSC

TEST CODE:          MSV             OPF             POSTL

1. DESCRIPTION:     Data Circuit

================================================================================

PAGE NUMBER:    59

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570744

ITEM NUMBER:        K7K

A. TYPE SERV: Ethernet Circuit

B. FROM:      OPF 1

C. TO:        SSPF Room 2377 TCMS Display Server

D. REMARKS:   Provide two (2) Ethernet circuits (#5ATU90363 and

#5ATU90365) between OPF 1 and SSPF Room 2377 TCMS

Display Server to support data transmission to

ASI/ALTEC personnel in Italy during MPLM/MSV post-

flight operations.  Technical Contacts: Andy Hunter

(867-5362), Jeff Levitt (867-5158), or Jim Brenner,

CSOC, (867-2056).

Reference:  Section 2734, Item K1G, DBR # 561051

Section 2755, Item K5K, DBR # 561052

Section 2755, Item K6K, DBR # 561056

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

RESPONDER: DON GARCEAU

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570745                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K8K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:15:09

REQUESTER:          KSC

TEST CODE:          MSV             OPF             POSTL

1. DESCRIPTION:     Data Circuit

A. TYPE SERV: Ethernet Circuit

B. FROM:      OPF 2

C. TO:        SSPF Room 2377 TCMS Display Server

D. REMARKS:   Provide two (2) Ethernet circuits (#5ATU90367 and

#5ATU90369) between OPF 2 and SSPF Room 2377 TCMS

Display Server to support data transmission to

ASI/ALTEC personnel in Italy during MPLM/MSV post-

flight operations.  Technical Contacts: Andy Hunter

================================================================================

PAGE NUMBER:    60

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570745

ITEM NUMBER:        K8K

(867-5362), Jeff Levitt (867-5158), or Jim Brenner,

CSOC, (867-2056).

Reference:  Section 2734, Item K1G, DBR # 561051

Section 2755, Item K5K, DBR # 561052

Section 2755, Item K6K, DBR # 561056

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

RESPONDER: DON GARCEAU

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570746                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K9K                           DATE LAST CHANGED:  03/06/03

SECTION:            2755                          TIME LAST CHANGED:  13:15:18

REQUESTER:          KSC

TEST CODE:          MSV             OPF             POSTL

1. DESCRIPTION:     Data Circuit

A. TYPE SERV: Ethernet Circuit

B. FROM:      OPF 3

C. TO:        SSPF Room 2377 TCMS Display Server

D. REMARKS:   Provide two (2) Ethernet circuits (#5ATU90315 and

#5ATU90316) between OPF 3 and SSPF Room 2377 TCMS

Display Server to support data transmission to

ASI/ALTEC personnel in Italy during MPLM/MSV post-

flight operations.  Technical Contacts: Andy Hunter

(867-5362), Jeff Levitt (867-5158), or Jim Brenner,

CSOC, (867-2056).

Reference:  Section 2734, Item K1G, DBR # 561051.

Section 2755, Item K5K, DBR # 561052.

Section 2755, Item K6K, DBR # 561056.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

================================================================================

PAGE NUMBER:    61

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2755 - VIDEO/DATA TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570746

ITEM NUMBER:        K9K

RESPONDER: DON GARCEAU

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    62

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2756 - VOICE RADIO TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552078                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2756                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF             TRANS

1. DESCRIPTION:     Provide portable UHF radios (Walkie Talkie)

Net 500/600 for use during MPLM/associated GSE unloading, transfer

and subsequent loading of the MPLM transportation container for

return to Italy.

REF        TYPE          QTY   NET/FREQ       PURPOSE

---------------------------------------------------------------------

1.1      UHF (Loan Pool)  15   As Assigned  MPLM/GSE Transport

Between SLF & SSPF.

Also return trip

from SSPF to SLF

for container loading.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: UB-E1

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  6 Unit only.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570747                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            2756                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          POSTL           SLF

1. DESCRIPTION:     Provide four (4) portable UHF radios (Walkie

Talkies), Net 500/600 for use during MPLM MSV runway tow

operations from the SLF to the OPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B2-E

================================================================================

PAGE NUMBER:    63

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2756 - VOICE RADIO TERMINATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570747

ITEM NUMBER:        K2K

RESPONDER: DEBII CALDWELL

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    64

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2760 - COMMUNICATIONS RECORDINGS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552079                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/10/03

SECTION:            2760                          TIME LAST CHANGED:  10:01:05

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Audio Recording

STA OR LOC:  SSPF

RECORD RQMT: Provide the capability to record Industrial Area OIS

Channels

START/STOP:  Start of test/activity to end of test/activity per OMI

or release by test conductor.

TIME CORRL:  Yes

REMARKS:     Record in accordance with Section 2750, Items K1KT

(DBR # 552072) and K2KT (DBR # 570740).

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552080                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/10/03

SECTION:            2760                          TIME LAST CHANGED:  10:01:24

REQUESTER:          KSC

TEST CODE:          OPF             PAD

1. DESCRIPTION:     Audio Recording

STA OR LOC:  OPF and Pad

RECORD RQMT: Provide the capability to record LC-39 Area OIS Channels

START/STOP:  Start of test/Activity to end of test/activity per OMI

or release by Test Conductor

TIME CORRL:  Yes

REMARKS:     Record in accordance with:

Section 2750, Item K3K, DBR # 552073

================================================================================

PAGE NUMBER:    65

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2760 - COMMUNICATIONS RECORDINGS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552080

ITEM NUMBER:        K2K

Section 2750, Item K4KT, DBR # 570742

Section 2750, Item K5KT, DBR # 570743

Section 2750, Item K6K, DBR # 570741

Section 2750, Item K7K, DBR # 570721

Section 2750, Item K8KT, DBR # 570720

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-102

RESPONDER: SYLVIA SEGURA

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/07/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552081                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/10/03

SECTION:            2760                          TIME LAST CHANGED:  09:53:57

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Video Recording

STA OR LOC:  SSPF

RECORD RQMT: Provide the capability to record specific Industrial

Area OTV cameras

START/STOP:  Start of test/activity to end of test/activity per OMI

or release by Test Conductor.

TIME CORRL:  Yes

REMARKS:     Reference:  Section 2800, Item K4K, DBR # 552087.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

RESPONDER: JEFF WALTERS

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    66

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2760 - COMMUNICATIONS RECORDINGS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552082                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/10/03

SECTION:            2760                          TIME LAST CHANGED:  10:37:15

REQUESTER:          KSC

TEST CODE:          PAD

1. DESCRIPTION:     Video Recording

STA OR LOC:  PAD

RECORD RQMT: Provide the capability to record LC-39 Area OTV cameras

START/STOP:  Start of test/activity to end of test/activity per OMI

or release by Test Conductor.

TIME CORRL:  Yes

REMARKS:     Reference:  Section 2800, Item K5K, DBR # 552088.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

RESPONDER: DAN HILL

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/10/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570748                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/10/03

SECTION:            2760                          TIME LAST CHANGED:  09:54:12

REQUESTER:          KSC

TEST CODE:          MPLM

1.  STA OR LOC:

2.  RECORD RQMTS:   Video

3.  AUD/VIDEO RCRD;

A. START:          Beginning of interior closeouts (Per IDS)

B. STOP:           Hatch closure (Per IDS)

C. AUDIO/VIDEO:    Video

D. SPEED:

E. REEL SIZE:

4.  TIME CORRL;

A. YES:            Yes

================================================================================

PAGE NUMBER:    67

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2760 - COMMUNICATIONS RECORDINGS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570748

ITEM NUMBER:        K5K

B. NO:

5.  REMARKS:        Record SSPF camera # 314, 24-hr. round the clock

for security reasons as follows:

Subject viewed: entrance to MPLM (close-up).

Over the weekends, use 72 hr tapes.  During the

week, use 24 hr tapes.  P/L Comm to retain tapes

for period of 60 days after launch.

Reference: Section 2800, Item K4K, DBR # 552087.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

RESPONDER: JEFF WALTERS

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570749                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/10/03

SECTION:            2760                          TIME LAST CHANGED:  12:30:58

REQUESTER:          KSC

TEST CODE:          OPF             POSTL           SLF

1.  STA OR LOC:     SLF to OPF

2.  RECORD RQMTS:   Provide capability to record video of Orbiter

convoy and MSV transfer from SLF to OPF.

3.  AUD/VIDEO RCRD;

A. START:          Beginning of transfer from SLF per OMI R09114V2

B. STOP:           End at MSV disconnect at OPF per OMI R09114V3

C. AUDIO/VIDEO:

D. SPEED:

E. REEL SIZE:

4.  TIME CORRL;

A. YES:            X

B. NO:

================================================================================

PAGE NUMBER:    68

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2760 - COMMUNICATIONS RECORDINGS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570749

ITEM NUMBER:        K6K

5.  REMARKS:        Camera  78 or 81.

Reference: Section 2800, Item K8K, DBR # 570751.

Data Disposition

Data         Time        Recipient/

Ref.  Type   Qty   Req'd       Remarks

-----------------------------------------

1     VHS     1    5 Working   Mike Dahm

Days      867-5132

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

RESPONDER: DAN HILL

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/10/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    69

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2780 - OTHER COMMUNICATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552083                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2780                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide 8 total Ethernet data interface

connections of PC Computers in the office area of SSPF to support

ASI/ALENIA E-Mail and file transfer capability with offices in MSFC,

JSC, and ITALY.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-304

RESPONDER: STEVE BUSBY

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Comments:  Please let me know the office ASAP!

Communications Support Request (CSR) will need to be

submitted by LSSM showing exact location of connection,

customer need date and how long connection will be needed.

The Payloads Operations Network (PON) is available 24 by 7, however

it is only supported M-F, 8:00am-4:30pm.  PON also has scheduled

maintenance the 1st and 3rd Thursday of every month during 2nd shift.

During these outages network connectivity is not guaranteed.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570750                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/10/03

SECTION:            2780                          TIME LAST CHANGED:  10:36:20

REQUESTER:          KSC

TEST CODE:          MSV             OPF             POSTL

1. DESCRIPTION:     Provide validation of existing phone lines for

861-1118 and 861-1119 at OPF Bay exterior MPLM Support Vehicle

(MSV) interface panel for MSV post-landing operations.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:    70

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2780 - OTHER COMMUNICATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    570750

ITEM NUMBER:        K2K

SUBSUPPLIER: SMI-KSC

RESPONDER: LAURIE LOCKRIDGE

SUBSUPPLIER COMMITMENT: WILCO      SEE RESPONSE          RESPONSE DATE: 03/07/03

RESPONSE:  Phone lines sill in place.  If a problem arises with the

phone lines, please contact 867-6346, then press 2.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    71

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2800 - VIDEO

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552085                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            2800                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          PAD             SSPF

1.  TYPE EQUIPMENT: Two (2) TV Monitors

2.  SUBJECT VIEWED: TCMS Test Data

3.  LOCATION:       User Room 2383 (No. 4)

4.  PERIOD:

5.  PURPOSE/

REMARKS:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552086                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            2800                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  TYPE EQUIPMENT: Television Monitor 25" Min.

2.  SUBJECT VIEWED:

3.  LOCATION:       Customer Management Room (2347)

4.  PERIOD:

5.  PURPOSE/

REMARKS:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:    72

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2800 - VIDEO

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552086

ITEM NUMBER:        K2K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    561057                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       10/26/01

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/10/03

SECTION:            2800                          TIME LAST CHANGED:  09:54:56

REQUESTER:          KSC

TEST CODE:          AAC-HT          DAP             PAD             PICO

POSTL           PRIT            SSPF

1.  TYPE EQUIPMENT: 3 CCTV Video Switcher Outputs

2.  SUBJECT VIEWED: MPLM

3.  LOCATION:       SSPF User Room 5 (2377)

4.  PERIOD:         During TCMS testing

5.  PURPOSE/

REMARKS:        To send video at ASI/ALTEC personnel in Italy

via JSC during TCMS testing at KSC.

Reference:  Section 2734, Item K1G, DBR # 561051.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

RESPONDER: JEFF WALTERS

SUBSUPPLIER COMMITMENT: WILCO      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  SSPF outputs 25, 31, and 32 for feed to Italy.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552087                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            2800                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  TYPE EQUIPMENT: OTV Cameras, 3 Required

2.  SUBJECT VIEWED: MPLM Test Area & Test Stand Area

3.  LOCATION:       High Bay Footprints 1 & 3

================================================================================

PAGE NUMBER:    73

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2800 - VIDEO

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552087

ITEM NUMBER:        K4K

4.  PERIOD:

5.  PURPOSE/

REMARKS:        Use of existing wall mounted video cameras in

the SSPF to monitor the TCMS test area.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552088                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            2800                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          PAD

1.  TYPE EQUIPMENT: OTV Cameras - Existing  (2 Required)

2.  SUBJECT VIEWED: MPLM

3.  LOCATION:       PCR Level and sides will be determined in the

Mission OR/OD

4.  PERIOD:         During MPLM testing

5.  PURPOSE/

REMARKS:        Required for observation of personnel and

Activities.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER:        CSOC-109

SUPPLIER COMMITMENT: NOACK                               RESPONSE DATE: 03/06/03

RESPONSE:  WILCO - USK-115/07-28-99.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    74

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2800 - VIDEO

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552817                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            2800                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SLF

1.  TYPE EQUIPMENT: Camcorder

2.  SUBJECT VIEWED: MPLM

3.  LOCATION:       SLF Tarmax

4.  PERIOD:         MPLM/GSE Arrival at KSC

5.  PURPOSE/

REMARKS:        To document MPLM arrival and subsequent

unloading operations and re-loading of the

Beluga Aircraft at the SLF.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Required support must be scheduled on the 72 hr/11 day

payload operations support schedule, allowing at least 24 hours

prior notification.  Tape dub disposition will be specified on the

same schedule entry.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552818                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/06/03

SECTION:            2800                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  TYPE EQUIPMENT: Camcorder

2.  SUBJECT VIEWED: MPLM

3.  LOCATION:       SSPF

4.  PERIOD:         MPLM/GSE Arrival at KSC

5.  PURPOSE/

REMARKS:        To document MPLM arrival and removal from the

================================================================================

PAGE NUMBER:    75

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 2800 - VIDEO

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552818

ITEM NUMBER:        K7K

shipping container at the SSPF airlock.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CSOC-601

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    570751                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      03/06/03

INITIAL DATE:       03/06/03

ITEM NUMBER:        K8K                           DATE LAST CHANGED:  03/10/03

SECTION:            2800                          TIME LAST CHANGED:  10:38:44

REQUESTER:          KSC

TEST CODE:          OPF             POSTL           SLF

1.  TYPE EQUIPMENT: OTV Cameras

2.  SUBJECT VIEWED: MSV in transit from SLF to OPF

3.  LOCATION:       VAB Roof, N.W. Corner

4.  PERIOD:         During MSV transport from the SLF to the OPF and

while at the OPF

5.  PURPOSE/

REMARKS:        Either camera 078 or 081 is needed to view the

MPLM Support Vehicle as it follows the Orbiter

Convoy from the SLF to the OPF.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: CSOC-109

RESPONDER: DAN HILL

SUBSUPPLIER COMMITMENT: WILCO                            RESPONSE DATE: 03/10/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    76

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3020 - REAL TIME DISPLAYS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552091                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            3020                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide four (4) consoles in SSPF User Room

#4 in support of MPLM testing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: UB-G2

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    77

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3100 - PHOTOGRAPHY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552092                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            3100                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          PAD             SSPF

1. DESCRIPTION:     Provide standard photo support for selective

operations including transportation, offloading, receiving,

inspections, processing, servicing, closeouts, etc.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: K264

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  KA91-F656 provides host mode operational and engineering

standard still photo support (35mm) on KSC for transportation,

offloading, receiving, and non-conformances only.  We also provide

digital imaging for Payload Ground Processing on KSC. First 250

photos/images standard.  Additional photography/imaging or local

service off KSC is available as an optional, non-standard service.

Also capable of scanning photographs/vu-graphs and providing digital

still images from VHS video tape.  To schedule, contact operations

engineering at 7-5800 or scheduling at 7-5598.  Questions: Call Al

Kinney at 867-5251.

PGOC does not provide photo support for International Space Station

Imagery Team requirements (processing, servicing, closeouts) as a

host mode service.  These are provided by the ISS Program Office and

should not be part of the PRD.  To schedule, contact Boeing scheduling

at 867-5598 and specify L&M Imagery.  Questions: Call Ed DeJulio at

867-5409.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    78

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552827                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     QG109KSC - General Processing Safety

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552828                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     QG07CKSC - ELSA Training

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552829                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     QF28XKSC - Industrial Area Familiarization

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:    79

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552829

ITEM NUMBER:        K3K

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552830                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     QF39XKSC - LC-39 Familiarization

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552831                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     OC320MDA - OIS-D Operational Intercommunication

System/OIS-D.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    80

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552100                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:         XC221BOE MPLM Concepts

3.  TYPE/SPECIALTY:

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Desired course for entrance to MPLM Processing

Areas and to work on MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552101                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:         QS205LSK How Clean is Clean Enough

3.  TYPE/SPECIALTY:

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for entrance to processing

areas and to work on MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:    81

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552101

ITEM NUMBER:        K7K

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552102                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K8K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:         Speciality MG212BOE - Scaffold Assembly and

Instruction

3.  TYPE/SPECIALTY:

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for personnel assembly and

construction of scaffolding for cargo processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552104                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K9K                           DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

================================================================================

PAGE NUMBER:    82

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552104

ITEM NUMBER:        K9K

2.  NUMBER:

3.  TYPE/SPECIALTY: QG223KSC Ammonia Hazardous Awareness

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for personnel access to the

MPLM Processing Area in the SSPF High Bay.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552095                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K10K                          DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:

3.  TYPE/SPECIALTY: QG271MDA - Fall Protection

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for personnel working on heights

above 4' and 6' from edge of platform in KSC

facilities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:    83

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552095

ITEM NUMBER:        K10K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552096                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K11K                          DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:

3.  TYPE/SPECIALTY: TG357MDA - AIr Bearing Pallets

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for personnel operating the air

bearing pallets in KSC facilities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552097                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K12K                          DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:

3.  TYPE/SPECIALTY: QG232KSC - Forklift Operations

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

================================================================================

PAGE NUMBER:    84

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552097

ITEM NUMBER:        K12K

5.  PURPOSE/REMARKS:Required course for personnel operating a KSC

forklift in KSC facilities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552098                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K13K                          DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:

3.  TYPE/SPECIALTY: TG340KSC - Crane Operations

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for personnel operating a KSC

crane within KSC facilities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552099                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K14K                          DATE LAST CHANGED:  03/06/03

SECTION:            3440                          TIME LAST CHANGED:  13:03:26

================================================================================

PAGE NUMBER:    85

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 3440 - OTHER TECHNICAL SUPPORT - TRAINING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552099

ITEM NUMBER:        K14K

REQUESTER:          KSC

TEST CODE:          N/A

1.  LOCATION:

2.  NUMBER:

3.  TYPE/SPECIALTY: TC290MDA - Rack Insertion Device (RID) - OIS-D

Operational Intercommunication System/OIS-D.

4.  DATE/DURATION:

A. ARRIVE:

B. DEPART:

5.  PURPOSE/REMARKS:Required course for personnel operating the

KSC RID.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: IDI-K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    86

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5200 - TRANSPORTATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552107                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5200                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide on-site transportation support for MPLM

hardware as required.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552108                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5200                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide receiving and inspection support for

receiving of MPLM hardware as required.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    87

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5300 - SERVICES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552262                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5300                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         General Facility Support

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/      FROM: L-13 Months

SERVICE:         TO:   R+2 Months

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide 8 Hr/Day, 5 Day/Wk support in SSPF

office, support and highbay areas.  Specific

areas include:

Facilities

- Access/security to SSPF highbay

- Access to office areas (lights/a/c)

- Network support

Tech Support

- Tools

- Equipment

- Consumables

Ops Desk Support

Logistics

- Parts/oru-s

Breakroom with:

- Microwave

- Refrigerator

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    88

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5300 - SERVICES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552263                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5300                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         General Systems Support

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/      FROM:  L-13 Months

SERVICE:         TO:    R+2 Months

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide 8 Hr/Day, 5 Day/Wk support in normal

facilities systems (i.e. power, a/c, gases/

fluids, temp./humidity control in highbay,

etc.) throughout time period of MPLM processing

in SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: M100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552111                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5300                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide ten (10) packages of lint free cloths for

use by ALENIA personnel during receipt of MPLM in SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

================================================================================

PAGE NUMBER:    89

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5300 - SERVICES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552111

ITEM NUMBER:        K3K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    90

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552264                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Provide eight (8) infrared heat lamps.

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Items required for installation of SVS targets

on the MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Only six (6) infrared heat lamps available.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552265                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Breakroom

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Breakroom will be required for approximately

================================================================================

PAGE NUMBER:    91

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552265

ITEM NUMBER:        K2K

12 techs and qual.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552266                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Customer Management Room

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide Conference Room 2347 with capacity for

20-25 persons for major MPLM tests.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Customer to schedule.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552267                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

================================================================================

PAGE NUMBER:    92

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552267

ITEM NUMBER:        K4K

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Conference Room

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Conference Room in SSPF with capacity for 20-25

persons for MPLM team.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552832                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Office Machine

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide fax machine with dedicated telephone

line in assigned office area of MPLM team.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:    93

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552832

ITEM NUMBER:        K5K

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552269                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Copying machine with auto feed, duplexing &

sort capability.

2. RA OR SA:

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  One (1) self-serve copy machine for use adjacent

to office and library areas of the ALENIA/ASI

Team.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552270                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

================================================================================

PAGE NUMBER:    94

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552270

ITEM NUMBER:        K7K

1. TYPE/ITEM

SERVICE:         Office Equipment

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Use of overhead projector for conference room

with screen.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552271                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K8K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Use of KSC reproduction services

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide main service and use of the reproduction

services for the ASI/ALENIA Team.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

================================================================================

PAGE NUMBER:    95

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552271

ITEM NUMBER:        K8K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552272                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K9K                           DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Office Space

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide permanent office space for ASI Resident

Office housing for two (2) people with securable

floor-to-ceiling walls and capable of holding

meetings (up to 6 people) and with standard

KSC services (power, telephones and network

(Ethernet data interface connections).

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552273                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K10K                          DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

================================================================================

PAGE NUMBER:    96

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552273

ITEM NUMBER:        K10K

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Office Space

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide office space with standard KSC services

(power, telephones and network connections) for

ten (10) ASI/ALENIA long-term temporary support

personnel.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Use available space in Rm 2257.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552274                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K11K                          DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Office Space

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide transient space for up to fifteen (15)

================================================================================

PAGE NUMBER:    97

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5310 - SERVICES - ADMINISTRATIVE, PERSONNEL, AND OFFICE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552274

ITEM NUMBER:        K11K

additional ASI/ALENIA support personnel during

MPLM delivery, off-load activities and other

processing activity.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Use available space in Rm 2257.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552275                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K12K                          DATE LAST CHANGED:  03/06/03

SECTION:            5310                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Office Fax Machine

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide dedicated fax machine with telephone line

in assigned office area of the ASI/ALENIA team.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:    98

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5311 - SERVICES - FIRE AND RESCUE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552276                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5311                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Safety Harnesses

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Ten (10) personnel safety straps/harnesses as

required.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552277                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5311                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Class 100,000 cleanroom garments, ESD

approved.

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide twenty (20) cleanroom garments for use

================================================================================

PAGE NUMBER:    99

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5311 - SERVICES - FIRE AND RESCUE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552277

ITEM NUMBER:        K2K

of MPLM personnel in the SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552278                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5311                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          PAD

1. TYPE/ITEM

SERVICE:         Class 100,000 cleanroom garments, ESD

approved.

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide ten (10) cleanroom garments for use by

MPLM personnel in the PCR.

SUPPLIER: KSC        ORG: KSC/PH-B        (KENNEDY SPACE CENTER              )

SUBSUPPLIER: USK-246

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552139                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5311                          TIME LAST CHANGED:  13:03:26

================================================================================

PAGE NUMBER:   100

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5311 - SERVICES - FIRE AND RESCUE

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552139

ITEM NUMBER:        K4K

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide 200 pair of cleanroom gloves that are

compatible with handling of electrostatic discharge sensitive items.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   101

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5314 - SERVICES - SECURITY AND SAFETY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552280                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5314                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          TRANS

1. TYPE/ITEM

SERVICE:

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide controlled, secure area around off-load

area of a 300-600 super airbus transporter Beluga

airplane at SLF with MPLM/GSE onboard.  Provide

chain and stanchions as required for controlled

area.  Provide security guard as required.

Provide access-list entry only to controlled area.

Provide three (3) car convoy-escort from SSPF to

SLF when SSPF operations are complete.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552281                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5314                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          TRANS

1. TYPE/ITEM

SERVICE:         Security Escort

2. RA OR SA:        SA

3. DATES, AMTS.

================================================================================

PAGE NUMBER:   102

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5314 - SERVICES - SECURITY AND SAFETY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552281

ITEM NUMBER:        K2K

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide security escort (2 or 3 cars as required)

for delivery of MPLM/GSE from the SLF to the SSPF.

MPLM/GSE will be air transported from the factory

to KSC by ASI/ALENIA.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552282                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5314                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          TRANS

1. TYPE/ITEM

SERVICE:         Security Access and Convoy Support

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide security access and convoy support of

overland incoming major flight elements.

Anticipated point of entry is KSC Gate 3.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:   103

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5314 - SERVICES - SECURITY AND SAFETY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552282

ITEM NUMBER:        K3K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552283                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5314                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          TRANS

1. TYPE/ITEM

SERVICE:         Security Escort

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide security escort (2 or 3 car as required)

for delivery of MPLM GSE from perimeter gate (TBD)

to the SSPF.  The MPLM GSE will be transported

from an arriving "local airport" to KSC by

customer provided flatbed trailer overland.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552146                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            5314                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          TRANS

1. DESCRIPTION:     KSC Safety Offices to monitor all hazardous

================================================================================

PAGE NUMBER:   104

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5314 - SERVICES - SECURITY AND SAFETY

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552146

ITEM NUMBER:        K5K

procedures and operations during MPLM/GSE off-load at the SLF

to completion of off-load and re-load or MPLM shipment container.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552147                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            5314                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          N/A

1. DESCRIPTION:     Badging and clearance service to support

permanently assigned and transient personnel in support of

MPLM Missions.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   105

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5320 - SERVICES - UTILITIES (ELECTRIC, WATER, AND SANITATION)

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552284                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5320                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Provide power carts w/10 circuits of 120V AC,

20A and 2 circuits of 208V AC, 30A

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Use of three (3) KSC 60 Hz power carts (PMN

GE5-00146) during all prelaunch testing of

MPLM in the SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N120

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552285                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5320                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Controlled Environment (CWA)

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:         Require tacky mats at control entrance to

Footprints 1 & 3.

================================================================================

PAGE NUMBER:   106

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5320 - SERVICES - UTILITIES (ELECTRIC, WATER, AND SANITATION)

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552285

ITEM NUMBER:        K2K

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Required for foot traffic debris removal before

entering MPLM processing areas.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: CMT/PASS

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552286                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5320                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Facility Power

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide facility power, 110/208 Vac, 3 Phases,

30, 60 or 100 Amperes to support FGSE operations

at the LPIS Footprint.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: M100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  The voltage level is 120/208 instead of 110/208.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   107

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5320 - SERVICES - UTILITIES (ELECTRIC, WATER, AND SANITATION)

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552152                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5320                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide a grounding cable to attach between the

MPLM and the SSPF facility ground.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N120

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552154                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            5320                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide electrical power from power conversion

technologies, Inc. GE5-00700 power supply to support MPLM work

on an as required basis.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N120

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   108

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5321 - SERVICES - HANDLING, STORAGE, AND DISPOSAL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552292                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5321                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Storage

2. RA OR SA:        RA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide environmentally controlled storage for:

- MDPS Containers

- MLI Storage Containers

Note per KSC LSSE:  The response given by

KA91-T942, dated 09-03-99 is a valid NOCMT.

No further action required.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L120

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Need sizes, quantity, stackable, etc.  Why do these empty

containers require environmental control?

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552293                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5321                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Storage of Flight Hardware

================================================================================

PAGE NUMBER:   109

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5321 - SERVICES - HANDLING, STORAGE, AND DISPOSAL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552293

ITEM NUMBER:        K2K

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Store up to (6) six emergency light power

supplies at a temperature of 0 to -4 deg.

centigrade.  Item to remain in storage until

required for the mission.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L120

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  PGOC warehousing does not have or meet this temperature

requirement.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    556943                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/14/00

INITIAL DATE:       09/14/00

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5321                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Storage of MPLM Batteries

2. RA OR SA:        RA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide storage area for three (3) MPLM flight

batteries; PN 19XLR40DC-3 (Yardney).  The weight

of each battery is 48 lbs and is 8" tall x 10"

deep x 12" wide.  The shipping container size and

================================================================================

PAGE NUMBER:   110

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5321 - SERVICES - HANDLING, STORAGE, AND DISPOSAL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    556943

ITEM NUMBER:        K3K

weight are unknown at this time.  Requirements

are for an air conditioned storage area that

meets flight hardware protection requirements.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L120

RESPONDER: TERRY TRAYLOR

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   111

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5330 - SERVICES - PROCUREMENT, SHIPPING, RECEIVING,  AND STOCK CONTROL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552287                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5330                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Procurement Service

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Use of procurement services as required in

emergencies.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552288                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5330                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Packaging Service

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide packing/crating/shipping services as

required.

================================================================================

PAGE NUMBER:   112

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5330 - SERVICES - PROCUREMENT, SHIPPING, RECEIVING,  AND STOCK CONTROL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552288

ITEM NUMBER:        K2K

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

RESPONDER: DEBBIE GAST

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Packing/Crating/Shipping.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552289                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5330                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Personnel

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide personnel to assist in element cleaning

operations as required before entry MPLM/GSE

entry into the SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G140

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552290                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

================================================================================

PAGE NUMBER:   113

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5330 - SERVICES - PROCUREMENT, SHIPPING, RECEIVING,  AND STOCK CONTROL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552290

ITEM NUMBER:        K4K

SECTION:            5330                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Tool Crib

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  MPLM personnel to have access to tool crib as

required for contingency needs.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552291                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            5330                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Emergency Spares

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Access to the KSC inventory for MPLM emergency/

contingency repairs and spares of support

================================================================================

PAGE NUMBER:   114

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5330 - SERVICES - PROCUREMENT, SHIPPING, RECEIVING,  AND STOCK CONTROL

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552291

ITEM NUMBER:        K5K

equipment and flight hardware.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   115

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5340 - SERVICES - PROPELLANTS, GASES, AND CHEMICALS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552168                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5340                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME/DESIG.:    Deionized Water

2.  MIL SPEC NO.:

3.  FED STOCK NO.:  N/A

4.  UNITS:          Gallons

5.  RA OR SA:       SA

6.  QTY REQD/QTR.:  Fifty (50)

7.  REMARKS:        Provide fifty (50) Gallons of high purity

deionized water, per SSP 305734.1-2.8.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552171                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5340                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME/DESIG.:    Isopropyl Alcohol 80/20 mix

2.  MIL SPEC NO.:   Standard TTI-735A, Grade A

3.  FED STOCK NO.:  N/A

4.  UNITS:          Gallons

5.  RA OR SA:       SA

6.  QTY REQD/QTR.:  One (1)

7.  REMARKS:        For use by processing personnel during MPLM

work for general purpose cleaning.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

================================================================================

PAGE NUMBER:   116

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5340 - SERVICES - PROPELLANTS, GASES, AND CHEMICALS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552171

ITEM NUMBER:        K2K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552172                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5340                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME/DESIG.:    Gaseous Helium

2.  MIL SPEC NO.:   SSP30537, Table 4.1 - 2.9, Grade A

3.  FED STOCK NO.:  N/A

4.  UNITS:          Cu. Ft.

5.  RA OR SA:       SA

6.  QTY REQD/QTR.:  5 Cu. Ft. AT 3000 psig (Max)

7.  REMARKS:        Facility gas at SSPF, required for leak checks in

support of MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   117

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5342 - SERVICES - CHEMICAL CLEANING

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552296                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5342                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  COMPONENT/SYS.;

A. NAME/DESCRIP:  Precision Cleaning Facility

B. QUANTITY:      SA

C. SPECIFICATION:

2.  CLEANING RQMT:

3.  SERVICE:

4.  REMARKS:        Provide facility and manpower to provide

precision cleaning on a contingency basis.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Support to be provided on a contingency basis and must

be within existing KSC capability.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   118

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552173                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Cargo Element Lifting Assembly (CELA)

2.  CAPACITY:       N/A

3.  PURPOSE:        Lift Cargo Elements

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      1

7.  REMARKS/

SPEC. INST.:    Use of CELA (PMN GH5-00622) to support following

moves:

MLPM transport container removal, MPLM removal

from shipping container and installation into

ERS.  Move to LPIS and installation into

canister prior to mission and removal after

the mission.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552174                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Cart (4 Wheel Flat Type)

2.  CAPACITY:

================================================================================

PAGE NUMBER:   119

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552174

ITEM NUMBER:        K2K

3.  PURPOSE:        Transport Flight & Support Equipment

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      1

7.  REMARKS/

SPEC. INST.:    Transport MPLM flight and support equipment from

receiving area in SSPF to assigned area for

inspection and/or storage as appropriate.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: TA-B3

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Four carts purchased and dedicated to CWA only for this

use.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552175                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Cargo Element Extension Kit (CEEK)

2.  CAPACITY:       N/A

3.  PURPOSE:        Aid in installation/survey of OSVS targets

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      1

7.  REMARKS/

SPEC. INST.:    Use of cargo element extension kit (PMN GH5-00717)

in LPIS stand for installation and survey of OSVS

targets.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:   120

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552175

ITEM NUMBER:        K3K

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552176                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Workstand air bearing pallets

2.  CAPACITY:

3.  PURPOSE:        Move cargo element into applicable workstand

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      One (1)

7.  REMARKS/

SPEC. INST.:    Use of one (1) workstand air bearing pallet

(PMN GX5-00023) in high bay to move sections

of MPLM into place.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552295                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

================================================================================

PAGE NUMBER:   121

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552295

ITEM NUMBER:        K5K

1.  NAME OR

NOMENCLATURE:   Cable Tray Support Stands

2.  CAPACITY:

3.  PURPOSE:        Use in test setup for MPLM processing.

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      Nine (9)

7.  REMARKS/

SPEC. INST.:    Use of nine (9) cable tray stands (PMN GH5-00712)

for MPLM PDV test setup area cable routing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552177                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Portable access stands

2.  CAPACITY:

3.  PURPOSE:        Used to access MPLM during processing in the

ERS and LPIS test stands (Pre and Post

mission).

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      Two (2)

7.  REMARKS/

================================================================================

PAGE NUMBER:   122

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552177

ITEM NUMBER:        K6K

SPEC. INST.:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552178                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Electric tow vehicle and 5th wheel dolly

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      One (1) each

7.  REMARKS/

SPEC. INST.:    Provide electric tow vehicle (PMN GX5-00129) and

5th wheel dolly to pull MPLM trailer into SSPF

airlock.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552179                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K8K                           DATE LAST CHANGED:  03/06/03

================================================================================

PAGE NUMBER:   123

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552179

ITEM NUMBER:        K8K

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Electric Forklift (PMN GX5-00875)

2.  CAPACITY:       8000 Lbs.

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) each

7.  REMARKS/

SPEC. INST.:    Provide 8000 lbs. forklift at SSPF to offload

MPLM TSE/SE at SSPF and move into airlock.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552180                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K9K                           DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          TRANS

1.  NAME OR

NOMENCLATURE:   Trailer (Air Ride)

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) each

7.  REMARKS/

================================================================================

PAGE NUMBER:   124

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552180

ITEM NUMBER:        K9K

SPEC. INST.:    Provide one (1) air ride trailer at SLF for

transport of MPLM SE from SLF to SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552181                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K10K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Hydrasets

2.  CAPACITY:

3.  PURPOSE:        Hoist MPLM

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:    Provide use of hydrasets for MPLM lifts in the

SSPF as noted.

(A) Initial lift of MPLM from shipping container

to ERS.

(B) Lift for moving MPLM from ERS to LPIS.

(C) Lift of MPLM from LPIS to canister.

(D) Lift of MPLM from canister to ERS.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:   125

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552181

ITEM NUMBER:        K10K

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552182                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K11K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Scaffolding

2.  CAPACITY:

3.  PURPOSE:        Use for access to MPLM.

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:    Scaffolding (PMN GE5P00626) requirement for MPLM:

o  Provide scaffolding (personnel access) and

handrail protection (deck level one), just

above or on the transportation handling

fixture surface.  360-Degree coverage is

highly desirable w/o reconfiguration.

o  Provide scaffolding (personnel access) and

handrail protection (Deck Level 2), approx.

60" but no more than 84" above deck level

one.  360-Degree coverage is highly

desirable w/o reconfiguration.

o  Provide cable strain relief above the APAS

approx. 72' above deck level 2.  360-Degree

coverage is high desirable.

================================================================================

PAGE NUMBER:   126

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552182

ITEM NUMBER:        K11K

o  Personnel access requirement will change

to accommodate test requirement.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552183                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K12K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Workstand air bearing casters

2.  CAPACITY:

3.  PURPOSE:        Move cargo element into applicable work area

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      A/R

7.  REMARKS/

SPEC. INST.:    Use of air bearing casters (PMN GX5-0023) in

Highbay to move sections of MPLM/GSE into place.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   127

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552184                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K13K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   Portable crane

2.  CAPACITY:       60 Tons

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER          Two (2) required

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:    One (1) 60 ton crane required for off-load of

Multi-Purpose Logistics Module (MPLM) associated

GSE and re-load of the MPLM shipment container.

The 2nd crane is for backup support.

NOTE:  Crane HE 202-036, P&H T-650 is identified

as the primary crane.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (SGS-062)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Scheduling without.

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   128

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552185                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K14K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   Portable Crane

2.  CAPACITY:       35 Ton

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      Two (2) units required

7.  REMARKS/

SPEC. INST.:    Required for off-load of MPLM/associated GSE and

re-load of the MPLM shipment container.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (SGS-062)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Scheduling without.

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552186                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K15K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF

================================================================================

PAGE NUMBER:   129

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552186

ITEM NUMBER:        K15K

1.  NAME OR

NOMENCLATURE:   Aircraft Tug

2.  CAPACITY:

3.  PURPOSE:        Capable of push/pulling of Beluga

4.  % USED:         Aircraft (maximum weight 155 tons)

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide one (1) aircraft tug with a maximum

height of 1.8 meters (5 feet, 9 inches) and

capable of push or pull movement of the

Beluga Aircraft.

NOTE:  An Aircraft Tug at Melbourne Airport

has been identified to meet the stated

requirement.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Scheduling and PRR.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552187                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K16K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   3 Meter height unloading platform

2.  CAPACITY:

3.  PURPOSE:        Unload from aft cargo bay of A300-600

4.  % USED:         sat "Beluga" Aircraft

================================================================================

PAGE NUMBER:   130

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552187

ITEM NUMBER:        K16K

5.  RA OR SA:

6.  NUMBER          One (1) set

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (SGS-062)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Platform not available.  Forklift is available and normally

used.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552188                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K17K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   2 Passenger stairs (5 meters height)

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER          Two (2) units

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:    Required for access into A300-600 Super Airbus

Transporter "Beluga" cargo bay.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:   131

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552188

ITEM NUMBER:        K17K

SUBSUPPLIER: (SGS-346)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552189                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K18K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   Aircraft ground power unit

2.  CAPACITY:

3.  PURPOSE:        Provide power to "Beluga"

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Required for support of MPLM/GSE delivery at SLF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (SGS-346)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   132

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552190                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K19K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:26

REQUESTER:          KSC

TEST CODE:          TRANS

1.  NAME OR

NOMENCLATURE:   Flatbed tractor trailer, 10 ft wide

2.  CAPACITY:       2.7 Tons (metric)

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER          One (1) each

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:    Provide one (1) air ride trailer for transport

of MGSE to SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Scheduling.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552191                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K20K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   Forklift

2.  CAPACITY:       Two (2) tons (metric)

3.  PURPOSE:        Support MPLM/GSE off-load activities

4.  % USED:

5.  RA OR SA:

6.  NUMBER

================================================================================

PAGE NUMBER:   133

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552191

ITEM NUMBER:        K20K

REQD/QTR.:      Two (2) each

7.  REMARKS/

SPEC. INST.:    Provide 2-ton (metric) forklifts for use in

MPLM off-load activity.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (TA-E1)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552192                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K21K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   Airport Trolley

2.  CAPACITY:

3.  PURPOSE:        Pallets handling

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER          One (1) unit

REQD/QTR.:

7.  REMARKS/

SPEC. INST.:    Standard airport type, approximately 5 meters

(16 feet) long, used for pallet handling during

MPLM/GSE unloading.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

================================================================================

PAGE NUMBER:   134

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552192

ITEM NUMBER:        K21K

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  T932 PGOC Transportation will provide tractor trailer.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552193                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K22K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SLF

1.  NAME OR

NOMENCLATURE:   Wooden spacers, donnage

2.  CAPACITY:

3.  PURPOSE:        Interface between ground and pallet

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      Required to support MPLM/associated GSE during

off-loading activities.

7.  REMARKS/

SPEC. INST.:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: (TA-E1)

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: BCMT

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552194                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K23K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

================================================================================

PAGE NUMBER:   135

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552194

ITEM NUMBER:        K23K

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of four (4) telescopic ladders or

equivalent with height capability of 3.5 meters (11.375 feet) or

more to reach the MPLM Trunnions/MPLM cover container clamps and

for the MGSE/FGSE unpacking.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552195                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K24K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide two (2) stepladders, approximately (18

inches) 45.8 cm high to facilitate work in the upper stand-off

areas of the MPLM interior.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552833                  REQUIREMENT STATUS: DELETED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/07/99

ITEM NUMBER:        K25K

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   136

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552197                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K26K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of two (2) pallet jacks with a

capacity of 200 kg (508 lbs) in support of MGSE unpacking/assembly.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G140

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552198                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K27K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Element Rotation Stand (ERS)

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide access and use of the ERS (GA1-01291)

during MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:   137

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552198

ITEM NUMBER:        K27K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552199                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K28K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Personnel Access Floor (PAF)

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide PAF (GA1-01324) to support MPLM

processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552200                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K29K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Hatch Restraint Fixture (HRF)

2.  CAPACITY:

3.  PURPOSE:

================================================================================

PAGE NUMBER:   138

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552200

ITEM NUMBER:        K29K

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide HRF (GN1-01248) to support MPLM

processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  HRF will be provided on MPLM.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552201                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K30K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Light Weight Floor (LWF)

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide LWF (GAAP00900) to support MPLM

processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:   139

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552201

ITEM NUMBER:        K30K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552202                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K31K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   PCBM/Hatch/AAC Pads and protective covers

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide support/use of PLBM/Hatch/AAC Pads and

protective covers during MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552203                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K32K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Aft access closure support fixture

2.  CAPACITY:

================================================================================

PAGE NUMBER:   140

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552203

ITEM NUMBER:        K32K

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:

7.  REMARKS/        One (1) unit

SPEC. INST.:    Provide support/use of the aft access closure

support fixture as required during MPLM

processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552204                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K33K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Hatch 1-G Kit

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide support/use of the Hatch 1-G Kit during

MPLM processing as required.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

================================================================================

PAGE NUMBER:   141

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552204

ITEM NUMBER:        K33K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552205                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K34K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Rack Insertion Device (RID)

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:

6.  NUMBER

REQD/QTR.:      One (1) unit

7.  REMARKS/

SPEC. INST.:    Provide support/use of the RID (GH5-00191)

during MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552207                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K35K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Electric forklift and operator

================================================================================

PAGE NUMBER:   142

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552207

ITEM NUMBER:        K35K

2.  CAPACITY:       6000-Lb

3.  PURPOSE:        To move incoming items to I-Bay and move heavy

equipment in SSPF.

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      One (1)

7.  REMARKS/

SPEC. INST.:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G140

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552834                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K36K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Overhead pendant crane with operator in I-Bay

to support testing.

2.  CAPACITY:

3.  PURPOSE:

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      AS Scheduled

7.  REMARKS/

SPEC. INST.:    Provide support of overhead pendant crane in

I-Bay with and operator in support of testing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

================================================================================

PAGE NUMBER:   143

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5351 - SERVICES - GROUND HANDLING EQUIPMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552834

ITEM NUMBER:        K36K

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Schedule through PDMS.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552209                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K37K                          DATE LAST CHANGED:  03/06/03

SECTION:            5351                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME OR

NOMENCLATURE:   Electric forklift and operator

2.  CAPACITY:       8,000 Lb

3.  PURPOSE:        To unload shipping containers from trailers

4.  % USED:

5.  RA OR SA:       SA

6.  NUMBER

REQD/QTR.:      One (1)

7.  REMARKS/

SPEC. INST.:

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  No 8K Electric Forklift available on KSC or CCAS.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   144

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5370 - SERVICES - AIR OPERATIONS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552211                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5370                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SLF

1. DESCRIPTION:     Provide aircraft support including use of the KSC

landing site, crash, fire support, and normal turnaround service

for landing and takeoff.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: SGS-347

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   145

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5380 - SERVICES - PHYSICAL AND LIFE SCIENCE EXPERIMENTS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552294                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5380                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Provide one (1) infrared pyrometers, range

0-200 Degrees F.

2. RA OR SA:

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Items required for installation of SVS targets

on MPLMs.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   146

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5410 - LABORATORY - CHEMICAL AND PHYSICAL ANALYSIS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552213                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5410                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  NAME/DESIG.:    Materials and Processing (M&P) support

2.  MIL SPEC NO.:

3.  DETAILS OF

ANALYSIS REQD:

4.  SAMPLING TIMES:

5.  REMARKS:        Provide use and personnel of the materials and

processing group for potential support on an as

required basis, in support of MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N230

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552216                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5410                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide mirrors, boroscope and endoscope for use

in the receiving inspection of the MPLM in the SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   147

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5420 - LABORATORY - SPECIAL ENVIRONMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552218                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5420                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Use of ESD table and floor mats along with wrist

stats for use in MPLM work area for handling ESD sensitive hardware.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G140

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552219                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5420                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide Pads and protective covers to protect

MPLM flight hardware during processing.

NOTE:  Request use of (PMN GP1P01290) GSE kit.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552220                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5420                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

================================================================================

PAGE NUMBER:   148

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5420 - LABORATORY - SPECIAL ENVIRONMENT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552220

ITEM NUMBER:        K3K

1. DESCRIPTION:     Provide portable lighting inside the MPLM with

sufficient illumination to work inside the MPLM and to allow visual

inspection.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   149

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5430 - LABORATORY - CALIBRATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552253                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5430                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of the following on an as required

basis.

- Multimeters

- Oscilloscopes

- Signal Generator

- Power Supplies

- Meg-Ohm Meters

- Hand Tools

- English System Wrenches

- Sockets

- Socket Drivers

- Screwdrivers

- Pliers

- Side Cutter Pliers

- Crimping Tools

- Soldering Equipment & Supplies

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552254                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5430                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of electrical load (PMN GE4-06039)

to dissipate 16 watts at 24 v dc for each ROFU PDA heater (2 units)

during the post delivery verification test (PDV).

================================================================================

PAGE NUMBER:   150

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5430 - LABORATORY - CALIBRATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552254

ITEM NUMBER:        K2K

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N120

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  We'll use whatever load we have available.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552255                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5430                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of a portable oxygen sensor to monitor

the air composition before entering inside the MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552259                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5430                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide Deutsch M15570-22-1 and Deutsch M15570-

16-1 tools for jiffy junction mating/demating connections to MLI/MDPS

ground connections during the MPLM processing on an as required basis.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L110

================================================================================

PAGE NUMBER:   151

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5430 - LABORATORY - CALIBRATION

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552259

ITEM NUMBER:        K4K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   152

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5440 - LABORATORY - TECHNICAL SHOPS AND LABS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552297                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Proofloading Capability

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide facility and manpower for proofloading

on a contingency basis in support of MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Support to be provided on a contingency basis and must be

within existing capability.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552298                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K2K                           DATE LAST CHANGED:  03/06/03

SECTION:            5440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Calibration Lab Service

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

================================================================================

PAGE NUMBER:   153

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5440 - LABORATORY - TECHNICAL SHOPS AND LABS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552298

ITEM NUMBER:        K2K

SPEC. INSTRUCT:  Provide facility and manpower for calibration

of support equipment and tools on a contingency

basis in support of MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Support to be provided on a contingency basis and must be

within existing capability.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552299                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. TYPE/ITEM

SERVICE:         Fabrication Facilities

2. RA OR SA:        SA

3. DATES, AMTS.

OR CHECK FOR

REQ'D ITEM/

SERVICE:

4. PURPOSE/REMARKS/

SPEC. INSTRUCT:  Provide facility and manpower to repair support

equipment on a contingency basis.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Support to be provided on a contingency basis and must be

within existing capability.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   154

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5440 - LABORATORY - TECHNICAL SHOPS AND LABS

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552212                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5440                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide facilities and manpower for mechanical/

electrical fabrication, modification and repair on a contingency

basis during MPLM processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: L100

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Support to be provided on a contingency basis and must be

within existing capability.

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   155

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552221                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/07/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide access to MPLM shipping container for

access cover removal, and attachment of MPLM to CELA.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: T384

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552222                  REQUIREMENT STATUS: DELETED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/07/99

ITEM NUMBER:        K2K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552223                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K3K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:

2.  TYPE FACILITY:  SSPF

3.  SITE DESIRED:   LPIS/ERS Stand

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Use of chain (plastic) for MPLM access during

SSPF processing operations.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G122

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:   156

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552223

ITEM NUMBER:        K3K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552224                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K4K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:       SSPF

2.  TYPE FACILITY:

3.  SITE DESIRED:   SSPF 2383

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide use of a User Control Room in the SSPF

by test personnel during all MPLM acceptance

testing and cargo element testing in the SSPF

and at the Pad.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: UB-G2

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552225                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K5K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:

2.  TYPE FACILITY:

3.  SITE DESIRED:

4.  STATION:        SSPF User Rooms 2387, 2393

5.  SCHEDULE:

6.  REMARKS:        Provide use of User Rooms 2387 & 2393 plus six

================================================================================

PAGE NUMBER:   157

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552225

ITEM NUMBER:        K5K

(6) tables and twenty (20) chairs for use by

test personnel during all phases of testing in

assigned User Rooms.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: UB-G2

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552226                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K6K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:       Offline Labs

2.  TYPE FACILITY:

3.  SITE DESIRED:   Room 1489 (1/2 of room)

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide room (Offline Lab type) to process SVS

targets for installation onto flight MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552227                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K7K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

================================================================================

PAGE NUMBER:   158

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552227

ITEM NUMBER:        K7K

1.  LOCATION:       MLI Repair Facility

2.  TYPE FACILITY:

3.  SITE DESIRED:   Room 1490 (1/2 of room)

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Use of MLI repair facility and services for

contingency repair or replacement of MLI

blankets used by MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N150

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Will provide use of MLI repair facility, services and

manpower for contingency.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552228                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K8K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          POSTL           SSPF

1.  LOCATION:       TCMS Support

2.  TYPE FACILITY:

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide test and check support from the TCMS

during all "power - on" MPLM processing

activities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: F262

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

================================================================================

PAGE NUMBER:   159

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552228

ITEM NUMBER:        K8K

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552229                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K9K                           DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:       SSPF

2.  TYPE FACILITY:  Provide the high bay overhead facility cranes

with operator on an as scheduled basis.

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide support of overhead cranes during MPLM

processing.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552230                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K10K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:       SSPF

2.  TYPE FACILITY:  Grounding straps

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide grounding straps and cables (PMN

================================================================================

PAGE NUMBER:   160

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552230

ITEM NUMBER:        K10K

GB5-00183) as required for processing activities

and hoisting operations for MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N120

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552234                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K11K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:       SSPF

2.  TYPE FACILITY:  Footprint

3.  SITE DESIRED:   Footprints 1 & 3

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide use of Footprints #1 and #3 for

processing of MPLM.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G122

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  Footprints 1 and 3 will be assigned to MPLM processing on

a primary basis.  However, floor space needs are derived from the

multiflow assessments and Footprints 1 and 3 may be temporarily

required for other flight hardware processing.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552235                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K12K                          DATE LAST CHANGED:  03/06/03

================================================================================

PAGE NUMBER:   161

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552235

ITEM NUMBER:        K12K

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          TRANS

1.  LOCATION:       TCF

2.  TYPE FACILITY:

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide the area, personnel and equipment to

accommodate the pressure cleaning of the MPLM

container in preparation for entry of this

container into the SSPF clean work area.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552236                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K13K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          TRANS

1.  LOCATION:       SLF

2.  TYPE FACILITY:  Shuttle Landing Facility

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide airport type tug for movement of airport

trolley during MPLM/GSE off-load activities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: BCMT

================================================================================

PAGE NUMBER:   162

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552236

ITEM NUMBER:        K13K

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552237                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K14K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of a vacuum cleaner or equivalent on

an as required basis during MPLM processing in the SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK      SEE RESPONSE          RESPONSE DATE: 03/06/03

RESPONSE:  INWORK - ECD 09-10-99.

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552238                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K15K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide orlan tape (or equivalent) bubble wrap,

and tyvek for installation to prevent damage to sealing surface

of the Common Berthing Mechanism (CBM).

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   163

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552239                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K16K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide mats for protection of the MPLM inside

before light weight floor (LWF)/personnel access floor (PAF)

installation and the - Z panel for tilting activities.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552240                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K17K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide KSC slings/shackles/rings as required to

open the MPLM container, MGSE unpacking/assembly.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552241                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K18K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

================================================================================

PAGE NUMBER:   164

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552241

ITEM NUMBER:        K18K

1. DESCRIPTION:     Provide use of the GHI-01248 Hatch 1-G Kit

during MPLM hatch opening.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552242                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K19K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide support of the Rack Insertion Device (RID)

and AAC End Effector to remove the Aft Access Closure (AAC).

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552243                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K20K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of the GR5-00866 Ground Air

Conditioning Unit (GACU) as required during MPLM processing in the

SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

================================================================================

PAGE NUMBER:   165

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    552243

ITEM NUMBER:        K20K

SUBSUPPLIER: E164

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552244                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K21K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide use of the GSA-02006 Gas Leakage Test

Stand (GLTS) as required during MPLM work processing in the SSPF.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: E164

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    552248                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       03/29/99

ITEM NUMBER:        K22K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Provide capability to lift and remove the cover

of the Micrometeoroids and Debris Protection System (MDPS) containers.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N100

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   166

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    556944                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/14/00

INITIAL DATE:       09/14/00

ITEM NUMBER:        K23K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1.  LOCATION:

2.  TYPE FACILITY:  Offline Processing Area

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide an offline processing area of

approximately 580 sq. ft. for processing Russian

flight hardware provided by Energia personnel.

Processing activity includes incoming cargo being

prepared for MPLM transportation to ISS and down

processing of cargo returning from the ISS via

the MPLM.  The following items are required to

support this activity:

A. Four (4) tables

B. Two (2) chairs

C. One (1) desk

D. One (1) desk chair

E. One (1) telephone

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G122

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

[PRD] DATABASE RECORD:    556945                  REQUIREMENT STATUS: APPROVED R

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      09/14/00

INITIAL DATE:       09/14/00

ITEM NUMBER:        K24K                          DATE LAST CHANGED:  03/06/03

SECTION:            5600                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

================================================================================

PAGE NUMBER:   167

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 5600 - FACILITIES

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

***CONTINUED***

[PRD] DATABASE RECORD:    556945

ITEM NUMBER:        K24K

1.  LOCATION:

2.  TYPE FACILITY:  Offline Processing Area

3.  SITE DESIRED:

4.  STATION:

5.  SCHEDULE:

6.  REMARKS:        Provide an off-line processing area of

approximately 580 sq. ft. for processing Russian

flight hardware provided by Khrunischer personnel.

Processing activity includes incoming cargo being

prepared for MPLM transportation to ISS and down

processing of cargo returning from the ISS via

the MPLM.  The following items are required to

support this activity:

A. Four (4) tables

B. Two (2) chairs

C. One (1) desk

D. One (1) desk chair

E. One (1) telephone

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: G122

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   168

CLASSIFICATION UNCLASSIFIED

CLASSIFICATION UNCLASSIFIED

L&L VOLUME III, PAYLOADS - MPLM (ANNEX SAQ)

PROGRAM REQUIREMENTS DOCUMENT/PROGRAM SUPPORT PLAN (PRD/PSP)

SECTION 6000 - OTHER SUPPORT

PUBLICATION DATE:  09/08/99    REVISION: 0000               RUN DATE: 03/18/03

============================================================================== =

[PRD] DATABASE RECORD:    552252                  REQUIREMENT STATUS: APPROVED

DOCUMENT ID:        SSL SAQ                       APPROVAL DATE:      07/28/99

INITIAL DATE:       07/28/99

ITEM NUMBER:        K1K                           DATE LAST CHANGED:  03/06/03

SECTION:            6000                          TIME LAST CHANGED:  13:03:27

REQUESTER:          KSC

TEST CODE:          SSPF

1. DESCRIPTION:     Alignment equipment as required.  Reference

PMN GK5-00756.

SUPPLIER: KSC        ORG: UB-C2           (K - KENNEDY SPACE CENTER          )

SUBSUPPLIER: N190

SUBSUPPLIER COMMITMENT: NOACK                            RESPONSE DATE: 03/06/03

------------------------------------------------------------------------------ -

================================================================================

PAGE NUMBER:   169

CLASSIFICATION UNCLASSIFIED

LAST PAGE OF REPORT

THIS REPORT CONTAINS   169 PAGES

------------------------------------------------------------------------------ -

REPORT BY: FORM=03  DOC=SSL SAQ APV= ALL  P1030=N