SDIS CHECKLIST

Draft ver 3 2/11/04

# PRE-MISSION INVENTORY

- NIKON Coolpix 5700 Camera

- Spare camera battery

- Battery Charger

- Camera to USB cord

- Camera Manual

- Tablet PC with stylus

- Tablet PC 110V electrical power cord

- Tablet PC 12V power supply

- ARNAV Transceiver

- ARNAV cable w/ 36 pin canon plug and DB9-USB adapter

- Phone (if required)

- Flashing Telephone Light

- Checklist

# PRE-MISSION BRIEFING

- Clarify Customer Needs

- Enter proper e-mail addresses in the Outlook Express Address Book

  - Double Tap Outlook Express ICON on desktop

  - Single Tap ADDRESSES Icon

  - Tap ADD a contact

  - Type the First Middle and Last Names

  - Type and verify e-mail address

  - Tap ADD

  - Tap OK

- Document communications requirements

- Plan the sortie

# PRE-MISSION SET-UP and OPS CHECK

- Install ARNAV transceiver to aircraft bracket

- Connect transmit and receive antenna cables – DO NOT REVERSE

- Connect cannon plug to RNAV unit and route to back seat

- Ensure all baggage will not interfere with cables

- Attach phone and / or visual phone light

- Attach ARNAV USB cable to outer USB port on tablet PC

- Perform an end-to-end test with all equipment when A/C is powered up

  - Take a picture

  - Download Picture

  - Crop picture

  - Send test e-mail

# AERIAL PICTURE TAKING

NOTE:  Camera battery saving power off will go into effect in 30 seconds – simply press DISP button (right thumb) to get power returned

- Camera Strap – around shoulder harness

- Lens  cap – Removed

- Mode Selector – CAMERA (right thumb)

- Power Switch – ON

- Viewfinder Display – ON

- If not on, press DISP button with right thumb

- Verify user set mode [1] in upper left of viewfiner or “C1” displayed in upper right of LCD when FUNC is pressed

  - NOTE:  User 1 is set for NO flash, 200 ASA, and infinite focus.

  - If don’t see [1] in viewfinder, hold FUNC button with right finger and rotate COMMAND DIAL until C.1 is shown in LCD display

  - Size – Check for FINE in LCD display

  - If not, press SIZE button (left finger) until it shows

- Pixels – Check for 2560 by holding SIZE button and rotating COMMAND DIAL until 2560 shows in LCD.

- Empty card should show 20 pictures available

- Take pictures as required

# QUICK REVIEW (IF DESIRED)

- Press QUICK button (right thumb)

- Scroll through pictures using MULTI-SELECTOR (right thumb)

- For full screen, press QUICK button again

- Press shutter HALF WAY to return to picture mode

# DOWNLOAD PICTURES TO PC

- Camera off

- Tablet PC up and running

- Attach USB cable to camera and to left PC USB port

- Turn camera on

- PC will recognize camera

- Select Copy pictures to a folder on my computer using Nikon View 5 (squiggle arrow)

- Select “Transfer all images” and select snake arrow

- Camera Off

- Disconnect Cord

# PREPARE PICTURES FOR TRANSMISSION

- Ensure NIKON VIEW program is active

- Select photo to crop by tapping once with stylus—Picture turns dark

- Select icon with a square with a pencil pointing into it (Edit Mode)

- Ensure Select Button on the right tool bar is active (upper left)

- Using stylus and stylus button, select the area of photo to crop

- If the wrong area is selected, use Edit Undo or Select None to fix mistakes

- When the proper area is highlighted, press the CROP button in lower left of tool bar (square with red dot)

- Open a file save box using the FILE and SAVE AS menus

- CHANGE the “Save as Type” to .JPG

- Select a new name for the cropped photo and save

- Exit Nikon Editer using red “X” in upper right corner

- Repeat for all photos needing to send

# PREPARING E-MAIL FOR TRANSMISSION

- Ensure in basic NIKON edit and pictures are present

- Select pictures to send by using CTRL tap with stylus

- (Note – typical e-mail should be 1 – 5 pictures)

- Select the ENVELOPE from the tool bar

- Ensure the REDUCE size to” box is selected and contains 750 pixels in width

- Select SEND

- Type in e-mail address – USE THE ADDRESS BOOK if at all possible

- Enter a subject line

- Enter a SHORT text message if needed

- Recheck addresses and text

- Press SEND

- Note:  SEND WILL PUT INTO OUTPUT SPOOLER.  AFTER A SHORT WHILE THE MESSAGE WILL MOVE INTO THE SATELLITE ICON ON LOWER SCREEN AND IT WILL BE RED MEANING A MESSAGE IS READY TO SEND.  IF THE ARNAV IS CONNECTED, IT WILL THEN TRY AND MAKE A CONNECTION AND SEND.  IF NOT, IT WILL PERIODICALLY CHECK FOR A CONNECTION AND SEND WHEN AVAILABLE.

CLEARING THE MAIL BUFFER WITHOUT SENDING

(Use this for training to ensure test messages are NOT sent)

- Double tap on the “Delete Mail Buffer” icon on desktop

- Satellite symbol on lower right tool bar should go GREEN (nothing to send)

# POST MISSION ACTIVITIES

- Document approximate satellite time in log (Note:  any phone calls will not register in the computer)

- Charge all PC and camera batteries as necessary

- Inspect equipment

- Clear photos from camera (save if needed on PC)

  - Press QUICK button twice

  - Scroll thru pictures – MULTI-SELECTOR

  - Press TRASH button

  - Press MULTI-SELECTOR down then right to delete each picture

- Delete old e-mail address from Outlook Express

- Equipment Inventory

  - NIKON Coolpix 5700 Camera

  - Spare camera battery

  - Battery Charger

  - Camera to USB cord

  - Camera Manual

  - Tablet PC with stylus

  - Tablet PC 110V electrical power cord

  - Tablet PC 12V power supply

  - ARNAV Transceiver

  - ARNAV cable w/ 36 pin canon plug and DB9-USB adapter

  - Phone (if required)

  - Flashing Telephone Light

  - Checklist

- Package and Secure Equipment