Handheld Devices Development Program Final Report

University of Alaska Anchorage Aviation Technology Division

May 11th, 2006

Handheld Devices Development Program Final Report

Grant Number 01-G-017

University of Alaska, Anchorage

Aviation Technology Division

May 11, 2006

Table of Contents

Part I:  Executive Summary	3

The team	3

Purpose	3

Background	3

Evaluation	4

Conclusion	4

Part II:  Hardware	5

PDA	5

Tablet PC	6

Data conversion	6

Part III:  Human factors	8

Turbulence	8

Placement of devices	8

Head down time	8

Part IV:  UAT Interface wiring diagrams	9

RS422/RS232	9

USB	10

UAT Interface wiring diagrams	11

Bluetooth	11

Part V:   Recommendations	12

PDA	12

Tablet PC	12

Interface	13

Part VI:  Cost	13

MFD	13

PDA	13

Tablet PC	13

Data converters	13

Software	13

Part VII:  Specifications	14

MFD	14

PDA	14

Tablet PC	14

Part VIII:  Acronyms	15

Handheld Devices Development Program Report Final

University of Alaska Anchorage

# Part I:  Executive Summary

## The team

The team was formed with a grant from the Capstone Program Office with the direction of Leonard Kirk, who is the Principal Investigator.  Michael Workman was appointed lead researcher and Marcus Holmquist assistant researcher for the task.  A diverse group of people from the aviation industry were consulted or aided in project tasks.

## Purpose

In support of the Federal Aviation Administration, Alaska Region Capstone Program, the University of Alaska Anchorage Aviation Technology Division Research Office has developed the test and evaluation plan for the purpose of using ADS-B portable technology. The goal was to conduct research and review of existing and developing technologies that may be adapted to general aviation use for acquisition of terrain, traffic and weather information from the ADS-B/UAT system.

## Background

In coordination with the on going Capstone safety initiative, the University of Alaska Anchorage Aviation Technology Division has been issued a grant, number 01-G-017 from the FAA Capstone Program Office to conduct research and review the existing and developing technologies that may be adapted to the general aviation community. This review entails an analysis of portable and or handheld technology which can interface with the ADS-B/UAT system in order to present terrain, traffic and weather information in the cockpit of general aviation aircraft. The goal is to demonstrate a system design that will allow a low cost handheld device to be coupled to an ADS-B system in a manner that will allow the maximum amount of information to be displayed in the cockpit. The UAA Aviation Technology Capstone research team has acquired several handheld devices and data converters for the interface to the ADS-B/UAT Garmin GDL-90.  Handheld GPS navigation software vendors were encouraged to participate in the display of ADS-B, TIS-B, FIS-B and weather using their software.

## Evaluation

Be advised this is a non-scientific study.  Much of the initial research was conducted via the internet using various means of research such as newsgroups, hardware reviews and equipment manufacture’s websites.  Several different models of handheld technology were purchased and reviewed as were the adapters for data conversion.  UAA has undertaken acquisition of navigational software from various vendors, tablet PC’s, personal data assistants (PDA’s), Garmin 296 moving map for reference as well as off the shelf components.  The team has integrated an interface in a Cessna 208B flight simulator to conduct initial evaluation of the handheld devices for usability in the cockpit. The handheld units were also evaluated for sunlight readability, weight, size and ease of use in a cockpit environment. Data interface from the Garmin GDL90 UAT was tested to demonstrate the feasibility of using various means of connectivity to the handheld devices i.e. Universal Serial Bus (USB), RS232 and Bluetooth.

Handheld units were demonstrated to the general aviation piloting community at trade shows and conferences for their input on the practicality of use in differing aircraft.

Navigation software from PCAvionics.com named MountainScope was used on all tested devices since it was the only software available that decoded all the data from the Garmin GDL90 UAT.

## Conclusion

The RS422 data interface from the Garmin GDL90 UAT to a handheld device proved successful.  The UAT was programmed to be in ‘Pass through’ mode for transmitting the data.  UAA demonstrated that data transfer via RS232, USB and Bluetooth are possible.  This allowed all handheld devices to receive information from the UAT.  The data from the UAT is a one-way transmission to the handheld, thus allowing the use of either a RS422 or RS232 adapter for conversion to USB.  RS232 was derived from using a portion of the differential output of the RS422 bus and providing a ground as reference to the unit or adapter. The main focus in the study was on RS232 and USB because the vast majority of the handhelds use these data formats for communication. The final data communication studied was Bluetooth.  With Bluetooth aircraft power is required, so a means of providing power will need to be incorporated by the installer.  Wireless Bluetooth worked marvelously; however, it requires a good working knowledge of how to setup communication ports and pairing for security so other computers can’t use the connection.

Sunlight readability was a main factor in determining which of the devices were suitable for use in the cockpit environment.  Most of the units failed to maintain readability in direct sunlight and were expunged from further evaluation.  A majority of the PDA’s passed mainly due to the transflective type screen.  The rest of the passing handhelds are expensive, however they are just as powerful as most high-end computers and could be used for many other purposes, helping justify the expense of acquiring the equipment.

When running on batteries, there always seems to be a concern of how much power is available.  To help alleviate this concern it’s advised to have some form of auxiliary aircraft power connection.  Also, all power management and screen saver functions need to be turned off for maximum performance which will result in a higher degree of power consumption.

Any device containing a hard drive for storage should be operated less than 10,000 feet as not to exceed manufacturer specification.  A majority of PDA’s use solid state memory without any altitude limitations.

Due to FAA certification issues handhelds are not a permanent part of the aircraft and must be installed in a manner to be readily removed.  UAA used a yoke style clamp with an articulating arm, but other means may be available. Careful installation of the wiring and secure mounting of the display is critical to maintain full movement of flight controls and avoiding being tangled in the wiring.

Flight testing with the UAT and various handheld technology is not complete due to restrictions of not having an approved interface connection for the Garmin GDL90 UAT.  UAA improvised using a remote Bluetooth GPS and a handheld for flight testing and a stationary UAT in the testing laboratory for communication testing.  The Capstone Office is currently working with Garmin for an interface connection that will use a RS232 connection.  Consequently the wiring shown in Part IV is for educational use only and may change as the product development continues.

# Part II:  Hardware

## PDA

The Personal Digital Assistant is the smallest and most economical of the handheld devices tested.  Display sizes range from three to four inches; this is a favorite of small and ultra light aircraft pilots.

Most of the PDA’s utilize a transflective type display technology helping with visibility in sunlight.  Several cockpit mounting options are available including cradles with communications via RS232 or wireless Bluetooth.

The clear leader of the PDA is the Hewlett Packard hx4700, however, this series is soon being discontinued.   The closest PDA to the HP is the Dell Axim X51v.

For database storage all the PDA’s require the addition of common inexpensive memory. A 1 gigabyte card will hold all of the North American Database.

The downside is anemic processing power and small screen size.  Mapping takes a few seconds to load when changing ranges and making a selection in turbulence on the small screen is difficult.  The operating system is Microsoft Windows Mobile Edition, which lacks many of the software features you get with a tablet PC.

The upside is that these units take up little space, weigh less than 8 ounces and have no problem running for long periods of time on battery.  Also a passive stylus or finger can be used for the touch screen functions, so if you drop the stylus your finger is a reliable backup.  The simple Microsoft Windows Mobile Edition makes it an easier unit to learn for novice users.

## Tablet PC

The Tablet PC is larger and more expensive.  These devices have more processing power than the PDA which gives them an edge on quickly displaying range changes and updating information.

The majority of the tablet PC category is unusable in direct sunlight.  A few have display technologies that help reduce sun glare or allow the sun to aid in brightness. Examples are Sony ‘Xbrite’ technology and the Motion Computing ‘View Anywhere’ display.

Memory storage is located on the internal hard drive, which has ample space for all the databases and programs.  The limiting factors are high altitude operations and or severe shock that may damage the hard drive.

The downside is that these units are power hungry, take up lots of space and weigh 1 to 2.5 pounds depending on model and battery size.  Most require the use of an active stylus, so your finger cannot be used to select on screen functions.  If the tablet PC is used on a network, remember, this makes the unit susceptible to viruses, worms, spy-ware and other common internet/network dangers.  The user should always perform a virus and spy-ware check before using in the cockpit or immediately after using the internet/network.

The upside is an easier to read display, menu selection functions appear larger and additional accessories such as a thumb track ball can be used.  Tablet PC’s generally have ample amounts of processing power and storage for all your piloting needs.  In many cases these handheld devices can be used for everyday computing which helps justify the additional cost.

## Data conversion

A note on RS232:  This mode of connectivity is no longer included with newer tablet PC’s, however, many of the PDA’s still utilize RS232. Newer PDA’s will soon use the new USB ‘On The Go’ standard of which will eliminate RS232 altogether on PDA’s.  Another technology is wireless Bluetooth which has been incorporated into almost all handhelds built to date thus pushing RS232 further into oblivion in the mainstream industries.  For the most part, USB is the accepted data interface for computers of today.  So the focus will be on converting the UAT RS422 data to USB and discuss Bluetooth briefly.  Keep in mind the data is a one way connection from the UAT via the data converter and then to the handheld device.

For the handheld devices at present, the Garmin GDL90 UAT produces ‘passthrough data’ via the RS422 bus so conversion will be one of the following:

RS422 to USB Company:  Vscom Model: USB-1COMI DB9 (9-pin male)

The differential transmission is converted to a USB signal and passed to the handheld device for reception.  A supplied Microsoft Windows driver is required to be installed in order for the unit to work.

RS422 to RS232 Company:  N/A       Model:  N/A

The simplest of the converters is wiring the negative half of the RS422 TX and providing a signal ground for the RS232 receiver reference signal.  We experienced no problems with this direct connection to a PDA.

RS422/RS232 to USB Company:  Vscom Model:  USB-1COM

By wiring the RS422 to be a pseudo RS232 as explained above one can use a RS232 to USB converter in place of the more expensive RS422 converter.  A supplied Microsoft Windows driver is required to be installed in order for this solution to work.

RS422 to Bluetooth Company:  Connectblue Model: cB-OEMSPA33i-01

Bluetooth requires the use of external power for operation.  The Connectblue unit operates between 8 and 30 volts and can use either RS422 or RS232, serving up to seven handhelds at the same time.  The advantage of using wireless technologies in the cockpit is mainly the reduction of wires and freedom of moving the unit around.  During testing our Bluetooth unit broadcast in excess of 300 feet to the handheld.  A security scheme called ‘pairing’ is used to avert others from using the same Bluetooth transmitter.  Certain steps need to be done on the users handheld equipment to prevent being seen or looking for other wireless networks.  This is beyond the scope of this report and is not discussed any further.

# Part III:  Human factors

## Turbulence

In light turbulence all of the devices were relativity easy to use.  With moderate or greater turbulence using the stylus at times caused incorrect selections to be made.  Some functions such as range changes utilize the handhelds buttons. Other common tasks can also be mapped to available handheld buttons.  A helpful solution was to add a small USB thumb track ball to control pointer movement, but this is only useable on the tablet PC’s.  It is suggested that the user preset and program the flight before airborne.

## Placement of devices

The universal solution is using a tubular clamp style attachment with an articulating arm.  This allows the user to place the handheld on the yoke in most aircraft, for others they may clamp on to any tubular structure.  The yoke seemed the most practical mounting location even for handhelds with the larger 8.4 inch screen.  Control loading didn’t seem to be a factor even with 2 to 3lbs of weight on the yoke.  Having the unit placed as part of your instrument scan is helpful and maintains continuity during flight.   Remember, handheld devices are not part of the aircraft and need to be installed so as not to be a permanent installation.  The use of items like Velcro, tape or rope is generally considered not to be an aircraft mounting device.  We are not saying to use these items but some users have.  Reference the applicable FAR and Advisory Circulars.  Such as FAR 43, FAR 91.21, AC 91.21-1a and AC120-76a

## Head down time

When the unit is first installed in the aircraft, many pilots may look at the handheld for longer periods of time because of the innovation of seeing other aircraft and weather.  As with most new things they become the norm and will be utilized as another tool for safety and shorter periods of head down time will occur.  What we observed was that by having the means of displaying traffic on a handheld, allowed the pilot to quickly establish the known aircraft and spend more time looking for any unknown obstacles.

# Part IV:  UAT Interface wiring diagrams

Simplified, for reference only

## RS422/RS232

UAT Interface wiring diagrams

Simplified, for reference only

## USB

## UAT Interface wiring diagrams

## Simplified, for reference only

## Bluetooth

# Part V:   Recommendations

## PDA

Hewlett Packard hx4700 series is best in class, mostly due to its larger screen size.  The next in line is the Dell Axim X51v.

## Tablet PC

Motion Computing LS800 with View Anywhere display is best in class.  Runner up being the Sony Vaio U750P (discontinued) replaced by the Sony Vaio UX180P which may be the clear winner with its bright touch screen display.  This unit was not tested as its release date is slated for July 2006.

## Interface

The RS232 to USB is the best all around connection for interface, considering the UAT will provide a true RS232 port in the near future.

# Part VI:  Cost

Dollar figures are approximate values, cost may vary.

## MFD

Garmin 396    $2,195.00

Garmin MX-20  $6,095.00

## PDA

HP hx4705   $595.00

Dell Axim X51v  $374.00

## Tablet PC

Motion Computing LS800 $2198.99

Sony Vaio UX180P  $1799.99

## Data converters

VScom RS422 to USB $49.00

VScom RS232 to USB $18.45

Connectblue Bluetooth  $245.00

## Software

PCAvionics MountainScope $495.00

# Part VII:  Specifications

## MFD

| Product name | Garmin 396 GPS | Garmin MX-20 |
| --- | --- | --- |
| Display type | 3.8 inch sunlight readable LCD | 6 inch sunlight readable LCD |
| Processor | ? | ? |
| RAM / ROM | ? | ? |
| Bluetooth | No | No |
| Battery life | 5+ hours @ max brightness | 0 hours requires external power |
| Weight | 14.2 ounces | 3.1 lbs |

## PDA

| Product name | Hewlett Packard hx4700 series | Dell Axim X51v |
| --- | --- | --- |
| Display type | 4 inch Transflective LCD Touch | 3.7 inch Transflective LCD Touch |
| Processor | Intel 624Mhz Xscale | Intel 624Mhz Xscale |
| RAM / ROM | 64MB / 128MB | 64MB / 256MB |
| Bluetooth | Yes | Yes |
| Battery life | 5+ hours @ max brightness | 4+ hours @ max brightness |
| Weight | 6.6 ounces | 6.2 ounces |

## Tablet PC

| Product name | Motion Computing LS800 | Sony Vaio UX180P |
| --- | --- | --- |
| Display type & resolution | 8.4 inch View Anywhere LCD Max 800 x 600 | 4.5 inch Xbrite touch LCD Max 1024 x 600 |
| Processor | Intel Pentium M 1.2GHz | Intel Core Solo 1.2GHz |
| RAM / HD | 512MB / 30GB | 512MB / 30GB |
| Bluetooth | Yes | Yes |
| Battery life | 2+ hours @ max brightness | 4.5 hours @ max brightness |
| Weight | 2.2 lbs | 1.1 lbs |

# Part VIII:  Acronyms

AC………………………………………...Advisory Circular or Aircraft

ADS-B……………………………………Automatic Dependant Surveillance-Broadcast

FIS-B……………………………………...Flight Information Service-Broadcast

GB………………………………………...Gigabyte

GDL………………………………………Garmin Data Link

GPS……………………………………….Global Position System

HD………………………………………...Hard Drive

HP…………………………………………Hewlett Packard

LCD……………………………………….Liquid Crystal Display

MB………………………………………...Megabyte

MFD……………………………………….Multi Function Display

PC…………………………………………Personal Computer

PDA…………………………………….....Personal Digital Assistant

PED………………………………………. Personal Electronic Device

RAM………………………………………Random Access Memory

ROM………………………………………Read Only Memory

TIS-B…………………………………..….Traffic Information Service-Broadcast

USB……………………………………….Universal Serial Bus

USB OTG…………………………………Universal Serial Bus On The Go

UAA……………………………………… University of Alaska Anchorage

UAT……………………………………….Universal Access Transceiver