POLAR Spacecraft Status As of: Tues, 27 Sept, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:51=AN STIP data only | NOAA-14J AM: 20:39=AN STIP data only | NOAA-15K AM: 18:06=AN GAC data only | NOAA-16L PM: 14:41=AN GAC&LAC data | NOAA-17M AM: 22:25=AN GAC&LAC data | NOAA-18N PM 14:00=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447. Array slew test 21-23 Sept |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily Plan to change to once per orbit | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (4/3/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=DTR 2B As of 21 Sept | SSRs 1,2,3,4,5 Current spikes TOAR 450 Plan SS switch to 5 b date TBD |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 | #1 ON 137.50 MHZ | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ Conflict with N14 | #2 ON 137.9125 MHZ Swap to #1 postponed until TBD |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 2 omni=rcp 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback Swapped 8/30 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback Swapped 8/30 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) Solar eclipse intermittently for 5 hours on 3 Oct 05 All spacecraft | ArrayOff +60 since 6/23/04 Full Sun Sun Angle 19 downtrend to 12 mid-Oct 05 Batts 1&2=LRC Batt !&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Considering move Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 8 downtrend to 2 degs on 10 Oct 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 49 Downtrend to 41 on 30 Oct 05 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Array 360 slew test occured 21 & 22 Sept Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Degraded Scan motor current surged 24 Sept bar. Worsened 27 Sept. Imagery bar codes Channels 2&4 APT | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Degraded Bar code imagery since 24 Sept TCE24 OFF 4/14/04 Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal TOAR 445 CLOSED 7/12/05 FW mode=Hi Powr FW Heater OFF | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | Operational Status downgraded to Yellow 15 Aug 05 TOAR 448 Noise in long wave channels 1-12. Increased degradation since 21 Sept |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 1 Pixel point error TOAR 452 closed operation is nominal |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU-8 TOAR 449 turned off 6/13 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop Autonomous TED shutdown 24 Sept commanded back on the same day | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations Transient anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Thermal downtrend occurring on spacecraft | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	 On 24 Sept (JDAY 267) engineers responded to a call from the POES controllers that a problem

had occurred with the N12 SEM.  After analyzing the situation it was noted that the SEM-TED autonomously shut off its high voltage at 07:43.  This is a known problem with pre-KLM SEMs that requires the TED be reinitialized.  A series of Command sent at 15:50z to recover the instrument.  The electron bias was commanded to level 2 inadvertently.  It was later commanded to level 5 (which was what users had stated the value had been prior to the shutdown). Prior to the anomaly the electron bias level telemetry read about 1.55 and after the recovery it read about 0.55.  On 26 Sept the CP was modified and another attempt was made to set the level to 5.   Once again the value did not match what it had been prior to the shutdown.  Therefore, the level was kept at this value while additional investigations into their settings are undertaken.  Another attempt to set the level to 3 on 27 Sept at 23:50z.

NOAA-14:	On 24 Sept (JDAY 267) at approx 11:21z (four hours after N12 SEM-TED lost synch) the N14 AVHRR experienced a

large scan motor current surge (up to 282 mAmps) with no corresponding surge in scan motor temp.  By 11:52z the same day, the scan motor current returned back to its nominal range of approximately 150 mAmps.  This surge caused bar codes to appear in AVHRR imagery which cleared up the next day at 07:30z when the MIRP rephase enable executed out of stored commands (as it does at this time each day).  Following its recovery, the scan motor remained nominal for the next several days (although it appeared to be operating in a wider range than in previous weeks).  However, early on 27 Sept, the scan motor current, this time accompanied by the scan motor temperature again surged to even higher levels where it has remained up to this time (illustration 1).  Imagery is now completely bar coded.  In response, plans are in effect which will enabled MIRP rephasing once per orbit over the South Pole (as it is done on N16) rather than only once per day at 07:30z.  This may help clear up some of the imagery.  The implementation of this change is scheduled to occur within the next week.

Battery voltage continue to run slightly on the low side (illustration 2). The power engineer is studying the efficacy of slightly decreasing the solar array offset in the coming days.  No plans are yet in place for such a move.

Discussions between EMOSS, NOAA and ORA engineers continue on the possibility of performing MSU end-of-life testing whereby spacecraft pitch rotation will be ceased for as long as one full orbit while the MSU continuously views deep space.  No date has been proposed for this test, nor has “final official approval” yet been forthcoming.  However, EMOSS engineers continue analyzing the risks and implementation strategies for performing such a test if and when it is approved.  For planning purposes only, the team is using a mid-November implementation data (while actual implementation must occur before ORA moves into NSOF.)

NOAA-15:	The N15 spacecraft remains in a thermal downtrend although which should continue as the sun angle on the spacecraft works its way down to approximately 2 degrees in mid-October.  The N15 AMSU’s were nominal during the past week (illustration 3) as was AVHRR and the HIRS (illustration 4). All other N15 subsystems including ADACS (illustration 5) were performing nominally, from an engineering perspective, at the time of this report.

NOAA-16:	The N16 AVHRR scan motor began to operate within a more erratic current range starting 20 Sept with spikes

beginning to occur on an irregular basis (illustration 6).  By 24 Sept (JDAY 267, the same day as N12 SEM and N14 AVHRR anomalies) bar codes began to appear on the imagery.  MIRP rephasing over the South Pole each orbit continues to correct the bar codes but at the current time this correction usually is not sustained for even a single orbit and so almost every GAC and HRPT image now contains at least some bar coding (illustration 7 and 8).  This anomaly has become somewhat typical of the N16 AVHRR which in the past two years has exhibited a variable cycle of degradation followed by improvement.  No actions or reconfigurations are planned to compensate for this situation.  The N16 AVHRR remains yellow in status and the TOAR written against it in Oct 2004 is closed.   Otherwise, the N16 HIRS was unchanged from last week (illustration 9) while the ADACS (specifically Y Gyro filtered data) became slightly more erratic as moon incursions into the earth sensor began to wane during the past two days (illustration 10).

NOAA-17:	There were no changes from last week.  The remaining N17 AMSU’s, the AVHRR and HIRS were all nominal and

stable during the past week (illustration 11 and 12).  In addition, the gyros on N17, which had recently shown some tendencies toward instability, remained generally stable during the past week (gyro-2 more so than gyro-1 see illustration 13).  Regardless, both the gyros on N17 are operating at, or near all time highs and increased vigilance over them will be maintained into the foreseeable future.

The safe state recorder on N17 was changed from DTR1B to DDR2B to better utilize the solid state recorders and free up one additional recorder.  This change was performed on 9/21/05 at 14:18:30.

NOAA-18:	The VTX transmitter (APT data) swap which was originally planned to occurred on 27 Sept has been postponed until

an as yet determined date.

The solar array 360 degree slew test was flawlessly implemented over the course of three days last week: 20 Sept (macro and spacecraft re-configuration loads), 21 Sept (360 degree reverse solar array slew), 22 Sept (360 degree forward solar array slew and reconfigure back to standard operating profiles).  In addition, EMOSS engineers provided data to NASA and factory engineers who have performed some preliminary analysis: Engineers did notice a difference in the frequency and the amplitude of the pitch attitude error during the slew but more analysis will be required before any conclusions can be drawn.

Another interesting sidelight from this test is that the N18 HIRS long wave channels, which had been improving in recent weeks, began to degrade starting at about the time of the first solar array slew on 21 Sept, a 360 degree reverse slew during the dark portion of the orbit lasting from 16:15:40 through 16:43:05z (illustration 14).   Analysis and discussion is ongoing at this time in trying to determine if the slew caused the HIRS degradation or if it was merely coincidence (or some of both).  Contrary to the first slew operation, there was no apparent coincidental change in HIRS channel noise that occurred during the second array test which ran on 22 Sept from 16:05:20 through 16:23:40z.  Furthermore, other than noise count increases on the HIRS long wave channels, neither of the slews appeared to have had any effect on the HIRS hardware and engineering values (i.e. filter motor current, housing temps etc).   Illustrations 15-25 provide some graphical depictions at a one second update rate of the effects of these array moves as they pertain to the HIRS, ADACS and EPS subsystems.  For more details on this situation go to the following web address:

http://www.orbit.nesdis.noaa.gov/smcd/spb/multisensor/hirs/.

N18 will have its safestate recorder changed in within the next week (although the actual date remains TBD).   The safe state recorder on N18 will be changed from DDR1B to DDR5B to better utilize the solid state recorders and free up one additional recorder.

Misc:	 A solar eclipse (moon blocking the sun) will be intermittently experienced by all POES spacecraft on 3 Oct between

07:35 and 13:27z.  Using the EMOSS eclipse model which has proven highly accurate in the past it was determined that no reconfigurations are necessary at this time.

Illustration 1:  NOAA-14 AVHRR Health Analysis

(Imagery bar codes resulted from the 24 Sept surge but after MIRP rephasing imagery returned to nominal.  However, since the big surge on 27 Sept, all imagery is bar coded. Data gaps caused by reduced number of N14 passes in recent days)

Illustration 2:  N14 Power Balance Analysis

(Battery voltages getting a little lower than desired although still well above undervoltage threshold.  Turning on APT data, not likely given the AVHRR anomaly, could change this equation.  Possibility of a small solar array offset move being recommended in the coming days.)

Illustration 3:  N15 AMSU Health Analysis

(Nominal with a continuing thermal downtrend which is expected to last for 1-2 more weeks.)

Illustration 4:  N15 HIRS and AVHRR Health Analysis

(Nominal and stable.)

Illustration 5:  N15 Attitude Control Health Analysis

(Generally nominal and historically stable, but will continue to be closely scrutinized by engineering, especially gyro-1.)

Illustration 6:  N16 AVHRR Health Analysis

(Degradation started on 20 Sept (JDAY 263) but bar code imagery didn’t become prevalent until 24 Sept.)

ILLUSTRATION 7:  N16 AVHRR Imagery Analysis

(Bar codes started on JDAY 267, 24 Sept, and have become more prevalent since.)

ILLUSTRATION 8:  N16 AVHRR GAC Analysis

(Prevalent bar codes but highly variable with or without MIRP rephasing.  X indicates where bar codes start.  In some case they go away without MIRP rephasing in others they require rephasing.  No synch delta plots are available this week because of problems with the archive system.)

ILLUSTRATION 9:  N16 HIRS Analysis

(Generally nominal and stable.)

Illustration 10:  N16 ADACS Analysis

(Generally nominal with some erratic performance in the Y_gyro filtered data as the spacecraft comes out of moon intrusion.)

ILLUSTRATION 11:  N17 AMSU Analysis

(Nominal and stable.)

Illustration 12:  N17 HIRS and AVHRR Analysis

(About the same as last week, nominal and stable.)

Illustration 13:  N17 ADACS Health Analysis

(About the same as last week.  EMOSS continues to closely monitor gyro performance.)

Illustration 14:  N18 HIRS Channel noise relative to Array Slew Test Implementation

(First instabilities occurred at about the same time as the first (longer) slew operation.  Coincidence or cause and effect?  Investigation is ongoing.

Illustration 15:  N18 Solar Array Drive Analysis for Test #1 on 21 Sept.

(Slew started at 16:15:40z and ended at 16:43:05z.  Nominal execution.)

Illustration 16:  N18 Solar Array Drive Analysis for Test #2 on 22 Sept.

(Slew started at 16:05:17z and ended at 16:23:00z.  Nominal execution.)

Illustration 17:  N18 Solar Array Drive SATCU data Analysis for Test #1 on 21 Sept.

(Slew started at 16:05:17z and ended at 16:23:00z.  Nominal execution.)

Illustration 18:  N18 Solar Array Drive SATCU data Analysis for Test #2 on 22 Sept.

Illustration 19:  N18 Solar Array Drive SATCU and Analog data Analysis for Test #1 on 21 Sept.

Illustration 20:  N18 Solar Array Drive SATCU and Analog data Analysis for Test #2 on 22 Sept.

Illustration 21:  N18 Solar Array Drive Test #1 on 21 Sept Relative to HIRS DIG-A telemetry samples

(No obvious effect on Filter Wheel Housing temps.  Similar outcome when analyzing the 22 Sept test. )

Illustration 22:  Additional HIRS Health Analysis short and long term views

(No obvious effect from the Array move tests on 21 & 22 Sept)

Illustration 23:  Test #1 (21 Sept) ADACS Health Analysis

Illustration 24:  Test #2 (22 Sept) ADACS Health Analysis

Illustration 25:  Side by side comparison of Rwheel speeds from each solar array test.

# Text boxes

Array

Test start