POLAR Spacecraft Status As of: Tues, 20 Sept, 16:00 EST

(changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:51=AN STIP data only | NOAA-14J AM: 20:39=AN STIP data only | NOAA-15K AM: 18:06=AN GAC data only | NOAA-16L PM: 14:41=AN GAC&LAC data | NOAA-17M AM: 22:25=AN GAC&LAC data | NOAA-18N PM 14:00=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 12/30/94 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 OBP1 inoperative | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU2 (XSU1 inop) | B-BUS XSU-1 | B-BUS XSU-1 XSU1 TOAR 444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO | NO |
| ADACS X=Yaw Y=Roll Z=Pitch | Nominal Mode RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Disabled Gyro chans=XYZ SS check Disabled when mode=YGC | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAA | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB Gyro-2 investigation | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447. Array slew test 21-23 Sept |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI BU random enables daily bias–7.0 mS | PRI daily bias -8 mS +100 mS 31Aug04 | PRI Daily Bias –5.5 mS -100 mS 31Aug04 | PRI Daily Bias –3 mS | PRI No daily bias |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 Daily | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 1 | 2 (since 4/23/03) 3 Channels inop | 2 since 4/18/05 | 1 Analog telem drifting | 1 |
| Recorders (DTR, SSR) Plan SS rec changes | DTRs 3A, 4, 5B Safestate 5B | DTRs 1, 2B, 5 Safestate- 1B | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=DTR 1B Switching safestate to #2B 21 Sept | SSRs 1,2,3,4,5 Current spikes TOAR 450 Plan safestate switch to 5b date TBD |
| VTX (APT data) | #1 ON 137.50 MHZ | OFF (nominal) Since 8/2/05 N17 conflict, turnon tbd | #1 ON 137.50 MHZ | INOP/Off OFF since 11/15/00 | #2 ON 137.62 MHZ Conflict with N14 | #2 ON 137.9125 MHZ Swap to #1 @ 137.1 planned NLT 27 Sept |
| BTX | #1 136.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 2 omni=rcp 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 3 – HRPT 2, 1 – Playback | 2-Omni HRPT Power drop TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback Swapped 8/30 4 – Playback 3 low power unused | 3 – HRPT TOAR424 low power 2 & 4 Playback 1-Standby STX-1 Power drop TOAR 443. | 1 - HRPT 3 - Playback Swapped 8/30 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, charge & V/T rates, eclipse states and sun angle) Solar eclipse intermittently for 5 hours on 3 Oct 05 All spacecraft | ArrayOff +60 since 6/23/04 Full Sun Sun Angle 19 downtrend to 12 mid-Oct 05 Batts 1&2=LRC Batt !&2 V/T=4 Shunt degraded SA CANT=37 degs | Array Off -55 Since 8/21/03 Considering move Eclipse all year Sun angle 48 Steady trend Batts 1-3= LRC Batts 1&3V/T=7/11 Batt2 VT=8/11 SS trigger =18.98 Shunt Degraded SA CANT=22 degs | Array Off -45 Since 1/25/01 Full Sun Sun Angle 8 downtrend to 2 degs on 10 Oct 05 Batts 1-3= LRC V/T=7/9 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 49 Downtrend to 41 on 30 Oct 05 Batts 1-3= LRC V/T=4/8 SA CANT=22 degs | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 68 Steady trend Batts 1-3= LRC V/T= 4/8 SA CANT=37 degs | Array Off. -40 Since 6/6/05 Array 360 slew test planned for 21 & 22 Sept Eclipse all year TOAR 453 on Batt C/D ratio Batts 1-3=LRC Batts 1-3 V/T=4/8 SADE -1 7/29/05 SA CANT=22 |
| AVHRR | Nominal | Nominal Channels 2 & 4 to APT 8/2/05 | Nominal Rare major scan motor surges. Last Incident 11/18/04 | Improving TCE24 OFF 4/14/04 Last bar code image 2 Sept. Waves Channel 3B only. | Nominal 3A-B switch enabled | Nominal 3A-B switch Disabled 8/05/05 Channel 3B only |
| AMSU-A1 |  |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| AMSU-A2 |  |  | Nominal | Nominal Space Position-2 | Nominal | Nominal Full scan mode |
| AMSU-B |  |  | Operational Bias in All Chans. Motor surges most recent 11/14/04 degraded data on Chan-3 since 4/30 | Operational Space Position-3 IPD reports channel 8 degradation | Nominal | Replaced by MHS |
| HIRS | OFF/Inop Turned off 6/23/05 For power balance Filter Wheel turned OFF 10/17/02. | NOMINAL Operational Occasional loss of Fwheel synch | NOMINAL Yellow status Since 16 May 05 FW Abrupt return to nominal TOAR 445 CLOSED 7/12/05 FW mode=Hi Powr FW Heater OFF | Operational High levels of imagery radiometric noise TOAR 441 open Occasional major FM surges, most recent 12/9/04 | NOMINAL 1 Pixel cross track misalignment . | Operational Status downgraded to Yellow 15 Aug 05 TOAR 448 Noise in long wave channels 1-12. Some improvement reported. |
| MHS/MIU |  |  |  |  |  | Nominal Space View=0 1 Pixel point error TOAR 452 closed operation is nominal |
| MSU | OFF/Inop Turned off for power balance 6/23/05 | Operational Scan motor and antenna problems End of life test plans underway |  |  |  |  |
| SSU |  | Nominal |  |  |  |  |
| DCS | Nominal | Nominal | Nominal | Nominal | Nominal | Nominal DRU’s 1-7 On DRU-8 TOAR 449 turned off 6/13 |
| SARR |  | Nominal | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | OFF Power Failure | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May |
| SEM | ON/Nominal Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 | Operational Elec-CH-HVPS=0 Prot-CH-HVPS=0 1 of 4 Tscopes inop | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=5 P-CDEM-HVPS=4 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=3 | Nominal Turned on 6 June at 14:05z |
| SBUV |  | Degraded Grate motor sticks Flex memory 3 (giant step) ops suspended 12/2/03 Reduced operations No data reported by products division 7/25/05 “transient” anomaly 1 Sept 05 |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops Procedure changes forthcoming | Nominal Anode mode since 6 July 13:30z |
| SADPOS |  |  | N/A | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | Nominal | TCE26 & 15H Telem invalid TOAR 432 HIRS FW Heat tuned ON 17 Apr and OFF on 18 Apr TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Thermal downtrend occurring on spacecraft | Nominal TCE24 OFF 4/14 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 TOAR 428 CLOSED 9/14/04 no corrective action possible. AMSU-A1 survival heaters on 10/29/03 | All TCE’s active |
|  | N12 | N14 | N15 | N16 | N17 | N18 |

COMMENTS/CHANGES:

NOAA-12:	No change from last week.  N12 supports have increased to average over one per day which improves the analytical

situation somewhat.  EMOSS Power subsystem engineer Carl Gliniak is not recommending any reconfigurations to the power balance equation at this time.

NOAA-14:	No changes since previous report.  The SBUV has operated nominally since its “transient anomaly” of 1 Sept while the

AVHRR continues to show signs of slightly less stability although it is still operating within nominal values

(illustration 1) and its imagery is still perfect. In analyzing the power balance situation on N14, EMOSS engineer Carl Gliniak is considering recommending a small reduction in the solar array offset (no more than 10 degrees to -45 from the current -55) in order to slightly increase power production which he has calculated to be just slightly less than optimum as battery voltages have started to dip below 20 volts upon exiting eclipse. The power survival safe state trigger set at 18.98 battery volts, which means that no N14 undervoltage trip appears imminent, at least as long as APT data (VTX transmitter) is not brought on line (there are no such plans in the offing).  This analysis has taken into account that the degraded shunts on N14 have been operating nominally and assumes that they will continue to do so after any array offset move (illustration 2).

EMOSS and NOAA engineers met with Tom Kleepies of ORA on Thursday 15 Sept to discuss his proposed end-of-life

test for the N14 MSU (described in last weeks report) whereby spacecraft pitch rotation will be ceased for as long as one full orbit while the MSU continuously views deep space.  No date has been proposed for this test, nor has “final official approval” yet been forthcoming.  However, EMOSS engineers are analyzing the risks and implementation strategies for performing such a test if and when it is approved.  For planning purposes only, the team is using a mid-November implementation data (while actual implementation must occur before ORA moves into NSOF.)  Jon Woodward, Jim Sheperd, Jim Walters Will Chadwick and Jeff Devine were POES team members supporting this meeting.

NOAA-15:	The N15 spacecraft remains in a thermal downtrend although which should continue as the sun angle on the spacecraft works its way down to approximately 2 degrees in mid-October.  The N15 AMSU’s were nominal during the past week (illustration 3) as was AVHRR and the HIRS (illustration 4). All other N15 subsystems including ADACS (illustration 5) were performing nominally, from an engineering perspective, at the time of this report.

NOAA-16:	The N16 AMSU’s, HIRS and AVHRR were generally stable and nominal during the past week (illustration 6).  The

N16 AVHRR actually improved with slightly lower scan motor currents and synch deltas that are no longer “pegging out”.  The result of this synch delta improvement has been that since 18 Sept, imagery is no longer showing the rephase frame loss (black line) over the South Pole because the rephase enable is no longer resulting in an actual MIRP rephase.    Furthermore, AVHRR imagery has not experienced a bar code since 2 Sept although wave patterns continue to persist (illustration 7).  The remainder of N16’s subsystems were also nominal and stable during the past week, from an engineering perspective.

NOAA-17:	There were no changes from last week.  The remaining N17 AMSU’s, the AVHRR and HIRS were all nominal and

stable during the past week (illustration 8).  In addition, the gyros on N17, which had recently shown some tendencies toward instability, remained generally stable during the past week (gyro-2 more so than gyro-1 see illustration 9).  Regardless, both the gyros on N17 are operating at, or near all time highs and increased vigilance over them will be maintained by EMOSS into the foreseeable future.  Jim Sheperd is EMOSS POC for this subsystem.

Per Procedure 050920.1330 generated and distributed by EMOSS engineer Will Chadwick:  The safe state recorder on N17 will be changed from DTR1B to DDR2B to better utilize the solid state recorders and free up one additional recorder.  Because DTR1B is the safe state recorder, it is not being utilized by scheduling and is reserved for TIP data recording should N18 enter safe state.  This recorder allows for 113 minutes of GAC data and 225 minutes of TIP data.  Changing the safe state recorder on N17 to DDR2B will allow for 360 minutes of GAC data and 2880 minutes of TIP data.  This change has two benefits due to DDR2B being about three times larger than DTR1B, it will allow for it to be used daily for regular recordings and have excess capacity should it be required to record TIP upon entering safe state.  See Table 7-6 from NOAA KLM P&CH for more information on recording/playback times for various DTR/DDR Modes and Sub modes.  The safe state recorder change will be performed on 9/21/05 during rev 16856 at Wallops at 14:18:30.  Will Chadwick has generated and distributed in preparation for this operation and is co-EMOSS POC for its implementation along with Jon Woodward

NOAA-18:	There were no changes to N18 configurations or health during the past week.  The N18 payload suite performed in a

nominal and stable manner (excepting HIRS channel 1) during the past week as did all the other subsystems (illustrations 10-13) relative to the known problems discussed in previous weekly reports.

The investigation into the pitch oscillation TOAR continues.  To support this investigation, a test that will slew the solar array 360 degrees (while in darkness) has been scheduled for 21 and 22 Sept starting at 14:30z,  outlined in Procedure 050916.1031 written by EMOSS engineer Jon Woodward and included in this Weekly Report (following this narrative).  The test will utilize both McMurdo and TDRSS to maximize the spacecrafts visibility while the array slew is in effect.  To ensure both assets could support the spacecraft EMOSS engineer Will Chadwick oversaw two successful data flow tests:  The first with McMurdo occurred on 12 Sept and the second with TDRSS occurred on 20

(N18 cont)

Sept.  Both tests turned on STX4 transmitter and configured AIP (at McMurdo) or TIP (on TDRSS) for continuous downlink which were successfully received by these sites and nominally transmitted back to SOCC.

The N18 APT data will be switched to VTX-1  (137.1 MHZ)  because VTX-2 (137.9125 MHZ), currently in operation, is often interfered with by cellular devises while orbiting over the European continent.  This change will be implemented NLT 27 Sept (actual date still TBD).  Will Chadwick is EMOSS POC.

Like N17 N18 will have its safestate recorder changed in within the next week (although the actual date remains TBD).  As per Procedure 050920.1230 written (but not yet distributed) by Will Chadwick:  The safe state recorder on N18 will be changed from DDR1B to DDR5B to better utilize the solid state recorders and free up one additional recorder.  Because DDR1B is the safe state recorder, it is not being utilized by scheduling and is reserved for TIP data recording should N18 enter safe state.  This recorder allows for 180 minutes of GAC data and 1440 minutes of TIP data.  Changing the safe state recorder on N18 to DDR5B will allow for 360 minutes of GAC data and 2880 minutes of TIP data.  This change has two benefits due to DDR5B being two times larger than DDR1B, it will allow for it to be used daily for regular recordings and have excess capacity should it be required to record TIP upon entering safe state.  See Table 7-6 from NOAA KLM P&CH for more information on recording/playback times for various DDR Modes and Submodes.

Misc:	 A solar eclipse (moon blocking the sun) will be intermittently experienced by all POES spacecraft on 3 Oct between

07:35 and 13:27z.  Using the EMOSS eclipse model which has proven highly accurate in the past, Will Chadwick has generated the predictions for this event as it relates to all POES spacecraft.  The bottom line is that no reconfigurations are recommended in preparation for this event.  See Illustrations 14a-f for the in-depth analysis used by EMOSS engineers to reach this conclusion.

Procedure Number: 050916.1031	   PREPARED BY: J. Woodward

SUBJECT/TITLE:	N18 full slew rotation

On Sept 20-22 NOAA-18 will be undergoing testing to help determine the cause of the pitch oscillations seen since launch.  The test involves commanding the array to slew speed where it will remain until it has completed a full revolution.  We will test both slew directions.  The slew period will be completed entirely during the darkness period of the orbit so that power levels and array health are unaffected.  Temporary changes will also be made to CPU telemetry to gather additional data.

One of the possible causes of the oscillations is the rotation of the solar array.  By placing the array in slew speed the characteristics of array rotation will be changed and if the signal changes, the array is responsible for the oscillations.

Day 1:

Beginning in the morning of Sept 20th (Jday 263), rev 1736 preparations for the test period are planned.  The changes to the CPU telemetry table will occur on this contact.  The first change will be for increased updates on solar array information.  The second affects MIMU raw telemetry.  It will replace the attitude error angle telemetry on the backup CPU.  In normal operations this will have no effect on spacecraft health since error angles are not computed on the backup CPU.  APTCHERR, AROLLERR and AYAWERR will read values that do not correspond to the actual error angles.

We plan on removing this change to the telemetry table when the testing is completed (1766 WAL, on 22 Sept).  However, if we switch CPUs during this period, the attitude error angles (assuming SCP1 is connected to BUS A, APTCHERR, AROLLERR and AYAWERR) will not read correct values.  Therefore, the CP to remove the telemetry changes will need to be run early.  The CP is named REMMIMTLM and it has a pass parameter.  The correct syntax to run the CP is:   CP START=REMMIMTLM C/N=C   This CP will return SCP 1’s CPU telemetry table to its nominal state. Also, the macros to complete the testing will be loaded this contact (but not activated).
Day 2:

The first testing will occur on 21st Sept (Jday 264), rev 1751 BAR.  The activities on this contact are to place the SATCU in mode A, turn on STX 4 (and configure for TIP), analog dwell on the Boom angle and begin the reverse slew test macro.  (Macro logic flows are included at the end of this document.)

The slew will take place after the Barrow (AOS 16:00z) contact once darkness is entered.  We will have TDRSS coverage for most of this portion of the test.  The currently scheduled time for coverage is 16:13z to 16:33z.  1751 McMurdo (16:46z) is scheduled, where we will revert to SATCU mode B.  The next CDA pass is rev 1752 WAL, where we will revert to normal DHS and COMM status (STX 4 off, and analog dwelling on the bus voltage).  This concludes testing for Day 1.

Operations wise, all CDA contacts will be taken on TCS1 as per normal.  However, we will have TCS2 set up for TDRSS and MCM data during those portions of the orbit.  The operations crew will set up the correct paths and sites for this period.

Day 3:

Day 3’s testing is very similar to Day 2’s.  The only differences between the two are that the slew will be in the forward direction, TDRSS coverage may not be available and the CPU telemetry changes will be removed at the conclusion of the test.  Times for CDA contacts are as follows:  Test activation at 1765 FBK (15:50z), monitoring at 1765 MCM (16:35z) and conclusion at 1766 WAL (17:16z).

Operations wise, all CDA contacts will be taken on TCS1 as per normal.  However, we will have TCS2 set up for TDRSS (possibly) and MCM data during those portions of the orbit.  The operations crew will set up the correct paths and sites for this period.

Macro logic flows:

Macro 9 Place the SAD in Reverse slew for 27.27 minutes 
If patch current less than 10, place SAD in ground control 
One second later, Enable macro 3 (safety macro) 
One second later, command SAD to reverse slew 
27.41 minutes later, return control to SADCS with SADPOS as backup

Macro A Place the SAD in Forward slew for 17.75 minutes 
If patch current less than 10, place SAD in ground control 
One second later, command SAD to forward slew 
One second later, Enable macro 3 (safety macro) 
17.67 minutes later, return control to SADCS with SADPOS as backup 

Macro B After 28 minutes place SADCS in control with SADPOS as backup 
Wait 28 minutes, return control to SADCS with SADPOS as backup

Illustration 1:  NOAA-14 AVHRR Health Analysis

(Less stable in recent days although imagery remains nominal.  Engineering is watching the trend closely.)

Illustration 2:  N14 Power Balance Analysis

(Battery voltages getting a little lower than desired although still well above undervoltage threshold.  Turning on APT data, not currently planned, could change this equation.  Possibility of a small solar array offset move being recommended in the coming days.)

Illustration 3:  N15 AMSU Health Analysis

(Nominal with a continuing thermal downtrend which is expected to last for 2-3 more weeks.)

Illustration 4:  N15 HIRS and AVHRR Health Analysis

(Nominal and stable.)

Illustration 5:  N15 Attitude Control Health Analysis

(Generally nominal and historically stable, but will continue to be closely scrutinized by engineering.)

Illustration 6:  N16 Primary Payload Motor Current Analysis

(Generally stable and possibly improved to a small degree on the AVHRR.)

ILLUSTRATION 7:  N16 AVHRR Imagery Analysis

(No bar codes since 2 Sept, and no MIRP rephase frame losses since 18 Sept now that synch delta has continued to improve. However, wave patterns still persist on HRPT images.)

ILLUSTRATION 8:  N17 Payload Motor Currents Analysis

(Generally nominal and stable.)

ILLUSTRATION 9:  N17 ADACS Analysis

(Generally nominal and stable.)

Illustration 10:  N18 Payload Motor Current Analysis

(Nominal and stable)

ILLUSTRATION 11:  N18 Battery Health Analysis (close-up)

(Engineers still investigating battery charge to discharge TOAR)

Illustration 12:  N18 DDR and Comm Analysis

(About the same as last week)

ILLUSTRATION 13:  N18 ADACS Health Analysis

(About the same as last eek.)

Illustration 14a:  N12 Eclipse Analysis (no reconfigurations recommended.)

Red asterisk on bottom plot indicates when N12 will experience “unexpected shadowing” (i.e. the effects of the eclipse).  Batteries start to discharge at approx 60% illumination intensity (or less) which is called “darkness threshold” for planning purposes.  Only one rev (at 08:45z see upper plot) will cause N12 to discharge its batteries and only for 6 minutes after which a quick and full recovery of this full sun spacecraft should result.  N12 has no SADPOS so autonomous takeover of the solar array is not a concern.  No yaw updates will occur during “deep eclipse” (20% intensity or less) so autonomous swap to YGC mode is not a concern.

Illustration 14b:  N14 Eclipse Analysis (no reconfigurations recommended.)

Red asterisk on bottom plot indicates when N14 will experience “unexpected shadowing” (i.e. the effects of the eclipse).  Batteries start to discharge at approx 60% illumination intensity which is called “darkness threshold” for planning purposes.  There are no revs where sun intensity will be low enough to cause N14 to discharge its batteries (upper plot).  N14 has no SADPOS so autonomous takeover of the solar array is not a concern.  No yaw updates will occur during any eclipse time frame so autonomous swap to YGC mode is not a concern.

Illustration 14c:  N15 Eclipse Analysis (no reconfigurations recommended.)

Red asterisk on bottom plot indicates when N15 will experience “unexpected shadowing” (i.e. the effects of the eclipse).  Batteries start to discharge at approx 60% illumination intensity (or less) which is called “darkness threshold” for planning purposes.  There are two revs where the sun intensity will go low enough to cause the batteries to discharge.  The most significant rev will be at 12:15z (upper plot) which will result in batteries discharging for approximately 7 minutes, which is not a concern.  N15 has no SADPOS so autonomous takeover of the solar array is not a concern.  No yaw updates will occur during any eclipse so autonomous swap to YGC mode is not a concern.

Illustration 14d:  N16 Eclipse Analysis (no reconfigurations recommended.)

Red asterisk on bottom plot indicates when N16 will experience “unexpected shadowing” (i.e. the effects of the eclipse).  Batteries start to discharge below (approx) 60% illumination intensity which is called “darkness threshold” for planning purposes.  Only one rev (at 11:20z, see upper plot) will cause N16 to discharge its batteries and only for 3 minutes after which a quick and full recovery should result.  N16 does have SADPOS enabled meaning at below 60% intensity (approx) a timer will start counting down from 12 minutes.  If greater than 60% intensity is not achieved within those 12 minutes, the timer expires and SADPOS will take control of the array and move it to 0 degree offset.  Since only 3 minutes of darkness are predicted, this provides a 9 minute margin of safety, considered more than ample by engineering because of the proven accuracy of the EMOSS model.  No yaw updates will occur during any part of the eclipse so autonomous swap to YGC mode is not a concern.

Illustration 14e:  N17 Eclipse Analysis (no reconfigurations recommended.)

Red asterisk on bottom plot indicates when N17 will experience “unexpected shadowing” (i.e. the effects of the eclipse).  Batteries start to discharge below (approx) 60% illumination intensity which is called “darkness threshold” for planning purposes.  Only one rev (at 09:36z, see upper plot) will cause N17 to discharge its batteries for 9 minutes after which a quick and full recovery should result.  N17 does have SADPOS enabled meaning that below 60% intensity (approx) a timer will start counting down from 12 minutes.  If greater than 60% intensity is not achieved within those 12 minutes, the timer expires and SADPOS will take control of the array and move it to 0 degree offset.  Since 9 minutes of darkness are predicted, this provides a 3 minute margin of safety, considered ample by engineering because of the proven accuracy of the EMOSS model.  No yaw updates will occur during any eclipse so autonomous swap to YGC mode is not a concern.

Illustration 14f:  N18 Eclipse Analysis (no reconfigurations recommended.)

Red asterisk on bottom plot indicates when N18 will experience “unexpected shadowing” (i.e. the effects of the eclipse).  Batteries start to discharge below (approx) 60% illumination intensity which is called “darkness threshold” for planning purposes.  Only one rev (at 11:45z, see upper plot) will cause N18 to discharge its batteries for 7 minutes after which a quick and full recovery should result.  N18 does have SADPOS enabled meaning below 60% (approx) intensity a timer will start counting down from 12 minutes.  If greater than 60% intensity is not achieved within those 12 minutes, the timer expires and SADPOS will take control of the array and move it to 0 degree offset.  Since 7 minutes of darkness are predicted, this provides a 5 minute margin of safety, considered ample by engineering because of the proven accuracy of the EMOSS model.  No yaw update will occur during any eclipse so autonomous swap to YGC mode is not a concern.

N17 Single Event Upset Scrub Log for the past 2 weeks and the entire mission

# POLAR SPACECRAFT TIP CLOCK ERROR

## WEEK ENDING September 16, 2005

| DAY/DATE | NOAA-12 | NOAA-14 | NOAA-15 | NOAA-16 | NOAA-17 | NOAA-18 |
| --- | --- | --- | --- | --- | --- | --- |
| FRI. 09/09 | -317 msec | +238 msec | -277 msec | +177 msec | +110 msec | +019 msec |
| SAT. 09/10 | -317 msec | +238 msec | -279 msec | +176 msec | +113 msec | +020 msec |
| SUN. 09/11 | -322 msec | +237 msec | -279 msec | +178 msec | +113 msec | +022 msec |
| MON. 09/12 | -321 msec | +243 msec | -281 msec | +178 msec | +114 msec | +023 msec |
| TUE. 09/13 | -321 msec | +244 msec | -283 msec | +178 msec | +114 msec | +027 msec |
| WED. 09/14 | -323 msec | +245 msec | -283 msec | +177 msec | +115 msec | +028 msec |
| THU. 09/15 | -825 msec | +246 msec | -284 msec | +179 msec | +117 msec | +028 msec |

EMOSS POC for this chart is JIM SHEPHERD

NOAA-14:  As of 12/23/03 the TIP clock is corrected daily by –7.0 msec to compensate for drift.

NOAA-15:  As of 04/22/03 the TIP clock is corrected daily by –8.0 msec to compensate for drift.

NOAA-16:  As of 12/23/03 the TIP clock is corrected daily by -5.5 msec to compensate for drift.

NOAA-17:  As of 12/23/03 the TIP clock is corrected daily by –3.0 msec to compensate for drift.

NOAA-12:  As of 12/10/03 the TIP clock is corrected daily by +6.5 msec to compensate for drift.

*    A clock jump of -500 milliseconds on 04/17/05 due to fractional second daily ETCUP. A clock

jump of +500 milliseconds on 07/01/05 due to fractional second daily ETCUP. Alternating +/-

500 millisecond clock jumps will ccur at 76-day intervals as long as fractional second daily

ETCUP is utilized to manage clock drift. The next +500 millisecond jump is expected on 09/15/05.

POES Engineering Contact List

Government

Renee Smith-Dearing  NOAA POES Constellation Lead 		301-817-4117

Dong Han:  NOAA, POES Payloads				301-817-4127

Mickey Fitzmaurice:  NOAA, POES Bus, IJPS	 	    	301-817-4016

Nicolaie Todirita (Todi): NOAA Ground Systems			301-817-4229

EMOSS-2 Contractor

Jeff Devine: EMOSS POES Lead 	 				301-817-4020

Jim Walters:  EMOSS, POES Payload Engineer			301-817-4033

Carl Gliniak, EMOSS POES Power and Thermal 			301-817-4207

Jim Sheperd, EMOSS POES Attitude Control			301-817-4030

Jon Woodward EMOSS, POES Flight Software C&CS		301-817-4019

Sally House EMOSS POES Payloads 				301-817-4026

William Chadwick EMOSS, POES Comm and DHS			301-817-4015