| Company Name: | Equipment/Job Identification: Joy 14CM Remote Controlled Continuous Mining Machine with attached Mobile Bridge Haulage Type of Equipment: Make: Model: Year: Use: |
| --- | --- |
| Mine Name: |  |
| Date of Analysis: |  |

# Pre-Assessment

### List pre-requisites here

Proper Equipment

General Safety Training

Ventilation Training

Knowledge of Fire Fighting

Knowledge of Escape Ways

Donning of SCSR

Knowledge of Roof Control Plan

Special Emphasis on Red Zone

Video “The Right Choice”

Knowledge of the Cutting Sequence

Good Attitude

# Duty 1: Start of Shift Activities

Learner will explain the importance of the start-of-shift activities. The learner will explain each job step, why they are conducted, any associated risk, and how to implement appropriate controls.  Start-of-shift activities include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Change clothes |  |  |  |  |
| Get CSE SR-100 |  |  |  |  |
| Check indicators |  |  |  |  |
| Check seal and dents |  |  |  |  |
| Remove from pouch monthly |  |  |  |  |
| Check in/Tag in |  |  |  |  |
| Obtain PPE |  |  |  | Gloves Safety glasses Hearing protection Safety boots Respirator Reflective material on clothing Hard hat |
| Get detector |  |  |  | Other detectors are available on the section |
| Check battery |  |  |  |  |
| Zero out |  |  |  |  |
| Get cap lamp with accessory receptacle |  |  |  |  |
| Check charger |  |  |  | On fully charged lamp, gauge will be off |
| Get streamers |  |  |  |  |
| Meet with foreman |  |  |  |  |
| Obtain work assignments |  |  |  |  |
| Discuss bolted/unbolted areas |  |  |  |  |
| Discuss planned belt-ups |  |  |  |  |
| Enter the mine |  |  |  |  |
| Conduct pre-op on mantrip |  |  |  | The miner operator normally operates the mantrip |
| Check lights |  |  |  |  |
| Ensure horn works |  |  |  |  |
| Check foot pedal brake |  |  |  |  |
| Check parking/emergency brake |  |  |  |  |
| Check fire Extinguisher |  |  |  |  |
| Get rock bar, pump jack, and handle |  |  |  |  |
| Check tires |  |  |  |  |
| Get on mantrip |  |  |  | Ensure mantrip has been pre-oped |
| Put on safety glasses before mantrip moves |  |  |  |  |
| Check travel way conditions |  |  |  | Always examine work area and work place for hazards |
| Tram mantrip to face Use dynamic brake when going downgrade |  |  |  |  |
| Travel at speed consistent with roadway conditions |  |  |  |  |
| Park out of the way |  |  |  |  |
| Set emergency brake |  |  |  |  |
| Turn power switch off |  |  |  |  |

# Duty 2:   Hot Seating

Learner will explain the importance of communicating and exchanging information as part of “hot seating (1st to 2nd shift) activities. The learner will explain each job step, why they are conducted, any associated risk, and how to implement appropriate controls.  Hot seating activities include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check travel way conditions |  |  |  | Always examine work area and work place for hazards |
| Talk to other continuous miner operator |  |  |  |  |
| Discuss condition of machine |  |  |  |  |
| Discuss problems with remote, shutdown switch, etc. |  |  |  |  |
| Discuss time frame for gas tests, if necessary |  |  |  |  |
| Discuss roof conditions |  |  |  |  |
| Discuss changes in bottom |  |  |  | Soft, wet and broken up |
| Examine roof and rib |  |  |  |  |
| Look for check curtains |  |  |  |  |
| Put red streamers up |  |  |  | Second row back and each side of the miner No one may go past streamers when miner is in cutting cycle |
| Check for unsupported roof signs |  |  |  | One should be placed behind the curtain Placed at all approaches to unsupported areas |

# Duty 3:   Starting Fresh

Learner will explain the importance of communicating and exchanging information as part of the “starting fresh (day shift) activities. The learner will explain each job step, why they are conducted, any associated risk, and how to implement appropriate controls.  The starting fresh (day shift) activities include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| Talk to mechanic on section |  |  |  | This is part of the required dust parameters examination. The mechanic will do these for you when possible. |
| Discuss water pressure |  |  |  | 25 PSI minimum |
| Discuss sprays |  |  |  | 17 sprays minimum per plan |
| Discuss bits |  |  |  |  |
| Discuss scrubber duct work and screen cleanliness |  |  |  |  |
| Discuss whether or not sump has been flushed |  |  |  |  |
| Talk with foreman |  |  |  | This is part of the required dust parameters examination |
| Discuss mining sequence |  |  |  |  |
| Discuss any problems observed |  |  |  |  |
| Discuss air readings and cut depths |  |  |  | 2 cut sequence 4 cut sequence |
| Obtain clearance to tram into the face |  |  |  |  |
| Confirm methane exam has been made |  |  |  |  |
| Tram miner to face |  |  |  |  |
| Allow foreman to take scrubber reading |  |  |  |  |
| Inform bridge crew where you are going and that you are starting up |  |  |  |  |
| Position yourself behind the miner in crosscut if at all possible |  |  |  | Stay out of miner red zones Discuss red zones for the continuous miner and MB’s |
| Position yourself in a crosscut ahead of the miner until it passes |  |  |  | Stay out of miner red zones Discuss red zones for the continuous miner and haulage |
| Start mining |  |  |  |  |

Duty 4:  Conducting Dust Parameter Exam

Learner will demonstrate how to conduct a safe and thorough dust parameter examination.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  A thorough examination includes the following job steps:

NOTE:  Some dust parameter exams may be completed in conjunction with continuous miner pre-op and starting fresh (day shift) activities.

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| De-energize miner |  |  |  |  |
| Put water pressure gage on right side of miner near bull wheels |  |  |  |  |
| Energize machine |  |  |  |  |
| Activate water sprays with remote |  |  |  |  |
| Count how many sprays are in operating condition |  |  |  | 17 operation sprays minimum No more than one blocked spray in each bar |
| Check scrubber sprays |  |  |  | Not part of the 17 – a minimum of two must be in operating condition at all times |
| Check blocker sprays |  |  |  |  |
| Check water pressure with the scrubber running |  |  |  | 25 psi minimum |
| De-energize miner |  |  |  |  |
| Remove the pressure gage |  |  |  |  |
| Clean out scrubber ductwork and screen |  |  |  | Remove demister cell and flush with water weekly Replace filter screen daily |
| Hose off top of miner |  |  |  |  |
| Energize miner |  |  |  |  |
| Check fire suppression |  |  |  |  |
| Report results to foreman |  |  |  | Foreman will initial box on side of miner. Foreman will verbally communicate results to other miners. Foreman will require mechanic to pitot the scrubber each shift |

# Duty 5:  Pre-op Continuous Miner

Learner will demonstrate how to conduct a safe and thorough pre-operational inspection of the Joy 14CM RC Continuous Mining Machine. Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  A thorough pre-operational inspection includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| De-energize and tag out machine at the load center | Prevent serious injury Miners known to start unexpectedly |  |  |  |
| Examine trailing cable | Prevent electrical shock, down time |  |  | Wear glove when handling cables |
| Look for Cuts | Prevent electrical shock, down time |  |  |  |
| Look for Nicks | Prevent electrical shock, down time |  |  |  |
| Look for Splices | Prevent electrical shock, down time Splices deteriorated over time |  |  | Count number of splices Splices must be more than 50’ from the miner No more than four splices at beginning of shift No more than five splices at end of shift |
| Walk around machine |  |  |  |  |
| Look for oil leaks |  |  |  |  |
| Look for missing parts/pieces |  |  |  |  |
| Check to ensure all lights are in place |  |  |  |  |
| Energize machine |  |  |  |  |
| Check to make sure all lights are working |  |  |  |  |
| Check all remote functions to ensure they are working properly | Avoid down time Could cause injury or death |  |  |  |

# Duty 6:   Tramming/Moving

Learner will demonstrate how to safely tram/move the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls. Safe tramming/moving the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check travel way conditions |  |  |  | Always examine work area and work place for hazards |
| Notify front mobile man that you are moving machine to the right side |  |  |  |  |
| Energize machine |  |  |  |  |
| Tram the machine | Machine can continue to move or move unexpectedly resulting in personal/crushing injuries |  |  | *CAUTION: THERE ARE TIMES WHEN THERE IS A SLIGHT DELAY WHEN YOU ACTIVATE THE TRAM LEVERS UNTIL THE MACHINE MOVES. CONTINUOUS MINERS CAN CONTINUE TO MOVE (DRIFT) AFTER CONTROL LEVERS ARE RETURNED TO THE NEUTRAL POSITION |
| Position yourself at the tail of the (RFM) (low belt) when moving around tail piece | Loss of employment, crushing injuries or death |  |  | Make sure belt is off (bridge crew will handle) See schematic |
| Shut miner down to move past miner | Loss of employment, crushing injuries or death |  |  |  |
| Move to the front of the miner when clear of belt tail |  |  |  |  |
| Position yourself in R1 outby crosscut | Loss of employment, crushing injuries or death |  |  | Can see in front of you and see bridge runner |
| Move slowly and allow bridges to catch up | Could cause injury to people and machinery |  |  | Caution around tailpiece and corners (High Risk areas for pinch points) |
| Move miner to R1 |  |  |  |  |
| Check with foreman to make sure workplace exam, gas test, and ventilation parameters exam have been done | Not done you lose time Build up of gas Bad roof |  |  | If the foreman has not made these exams, you are required to make the exam - if in doubt, make exam |
| Bridge operators will watch the antennas |  |  |  | Antennas are slide markers |
| Bridge operators will move in coordination with the continuous miner |  |  |  | When slide markers are close to 4’ apart, the bridge operator needs to close the gap |
| Reposition yourself in R2 when mining R2 |  |  |  |  |
| Method 1 of tramming to the left |  |  |  |  |
| Notify front mobile man that you are moving machine to the left side |  |  |  | Miner operator needs to continuously communicate with the bridge crew |
| Position yourself beside tail of the RFM (low-belt) inby the bits of the miner |  |  |  | See schematic |
| Back continuous miner along the RFM until you can turn into the backhole |  |  |  |  |
| Flag front mobile man and jog coal chain once before tramming towards L2 |  |  |  | Jogging the coal chain informs the bridge operator the miner is going to stop and go in the other direction |
| Swing miner into crosscut between belt and L1 |  |  |  |  |
| Shut miner down to move past miner |  |  |  |  |
| Crawl past miner into L1 |  |  |  |  |
| Position yourself in L1 outby |  |  |  |  |
| Move into L2 inby bits as miner approaches L1 |  |  |  | Be aware of blind spots. You must stay inby the continuous miner to do this. |
| Check with foreman to make sure workplace exam, gas test, and ventilation parameters exam have been done | Not done you lose time Build up of gas Bad roof |  |  |  |
| Method 2 of tramming to the left |  |  |  |  |
| Notify front mobile man that you are moving machine to the left side of the section |  |  |  | Mine operator needs to continuously communicate with the bridge crew |
| Position yourself beside tail of the RFM (low-belt) inby the bits of the miner |  |  |  | See schematic |
| Back continuous miner along the RFM until you can turn into the backhole |  |  |  |  |
| Flag front mobile man and jog coal chain once before tramming towards L2 |  |  |  |  |
| Swing miner into crosscut between belt and L1 |  |  |  |  |
| Shut miner down to move past miner |  |  |  |  |
| Crawl past miner into L1 inby |  |  |  |  |
| Tram past L1 up to L2 |  |  |  |  |
| Shut miner down |  |  |  |  |
| Crawl past miner into L2 outby |  |  |  |  |
| Check with foreman to make sure workplace exam, gas test, and ventilation parameters exam have been done | Not done you lose time Build up of gas Bad roof |  |  |  |
| Method 3 of tramming to the left |  |  |  |  |
| Notify front mobile man that you are moving machine to the left side |  |  |  | Miner operator needs to continuously communicate with the bridge crew |
| Position yourself beside tail of the RFM (low-belt) inby the bits of the miner |  |  |  | See schematic |
| Back continuous miner along the RFM until you can turn into the backhole |  |  |  |  |
| Flag front mobile man and jog coal chain once before tramming towards L2 |  |  |  |  |
| Swing miner into crosscut between belt and L1 |  |  |  |  |
| Continue tramming until you reach crosscut between L1 and L2 |  |  |  |  |
| Shut miner down to move past miner |  |  |  |  |
| Crawl past miner into L2 outby |  |  |  |  |
| Check with foreman to make sure workplace exam, gas test, and ventilation parameters exam have been done | Not done you lose time Build up of gas Bad roof |  |  |  |
| Use Method 1 when going to L1 |  |  |  |  |

# Duty 7:   Cutting Coal

Learner will demonstrate how to safety and efficiently cut coal with the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient cutting of coal with the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| Position yourself to cut coal |  |  |  | Red zone pattern changes while cutting coal and depending on the entry you are in See diagram on mining sequences Stay out of miner red zones Discuss red zones for the continuous miner and haulage Never allow anyone to be inby your physical position while cutting coal |
| Take right side cut |  |  |  | You need to conform to red zone outline |
| Standing on the right side of the machine |  |  |  | You need to conform to the red zone outline Caution: Do not stand directly behind the conveyor of the miner – the conveyor chain can propel rock and coal at grate speed and pressure |
| Standing on the left side of the machine |  |  |  | Noise and dust exposure may be much greater standing on the scrubber side of the machine. You need to conform to the red zone outline Caution: Do not stand directly behind the conveyor of the miner – the conveyor chain can propel rock and coal at grate speed and pressure |
| Take left side cut |  |  |  | You need to conform to the red zone outline |
| Position yourself outby the streamers on the right side of the miner |  |  |  | You need to conform to the red zone outline |
| Maintain as much distance from miner as possible to avoid pinch points and still be able to maintain width |  |  |  | You need to conform to the red zone outline |
| Turn sprays on | Health consideration Methane consideration Motors are cooled with spray water Could cause down time |  |  |  |
| Activate scrubber |  |  |  |  |
| Start cutter heads |  |  |  | Be back away from the face |
| Put in high tram |  |  |  |  |
| Start coal chains |  |  |  |  |
| Pull heads up |  |  |  |  |
| Nick roof |  |  |  |  |
| Look for white smoke |  |  |  |  |
| Listen for change in sound |  |  |  |  |
| Sump in for 2-1/2 feet |  |  |  |  |
| Drop heads |  |  |  |  |
| Let them mill around for approximately 5-6 seconds |  |  |  |  |
| Tram miner back until you see the heads fall on the bottom |  |  |  |  |
| Tram straight back in until you hit the face |  |  |  |  |
| Pull heads to the roof, sump in, begin mining |  |  |  |  |
| Advance curtains within 25’ of machine |  |  |  | Operator must always be outby the end of the curtain Curtain may only be advanced to the streamers while cutting |
| Repeat cycle until your reach 40’ mark |  |  |  |  |
| Flag front mobile man that you are coming back |  |  |  |  |
| Shut down the following machine functions |  |  |  |  |
| Cutters |  |  |  |  |
| Coal chain |  |  |  |  |
| Scrubber |  |  |  |  |
| Sprays |  |  |  | Sprays need to remain on for at least 10 seconds after cutter heads are shut down |
| Back out of cut |  |  |  |  |
| Take curtain down enough to back miner out |  |  |  |  |
| Back miner outby streamers |  |  |  | Be aware of pinch points Tips of bits Rear corner of machine |
| Hang unsupported roof signs | Prevents people from unintentionally going under unsupported roof |  |  |  |
| Clean scrubber screen |  |  |  |  |
| Pull the screen |  |  |  |  |
| Tap it clean |  |  |  |  |
| Replace screen and close door |  |  |  |  |
| Conduct gas check every 20 minutes | Failure to take gas test could allow methane to accumulate Ignition hazard |  |  | Use Gizmo May be able to take complete cut within the 20 minute interval |
| Hang curtain to the last row of bolts | Failure to hang curtain could cause methane to accumulate |  |  |  |
| Signal bridge crew with cap lamp that you are going to move to the left side |  |  |  | Discuss signals for “come ahead”, “come back”, etc. Never cross over or under a bridge until the bridges are on the bottom and shut down. |
| Position miner to left side |  |  |  |  |
| Repeat cut cycle until left side has been removed |  |  |  |  |
| Cleanup cut |  |  |  |  |
| Make two to three passes |  |  |  |  |
| Signal bridge crew each time you move |  |  |  |  |
| Make gas check for bolters | Roof Bolters would have to make gas check with 40’ probe slowing them down |  |  | Use gizmo |
| Pull streamers on the way back out |  |  |  |  |
| Notify bolters of time gas check was taken | Failure to notify the bolters would require them to make another gas check |  |  |  |
| Thoroughly wash out scrubber screen before repeating cycle |  |  |  |  |

# Duty 8:   Turn crosscut to the Right

Learner will demonstrate how to safely turn right crosscuts with the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage (belt to R1 and L2). Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Procedures for safely turning right crosscuts with the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage will include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| Ensure workplace exam, gas tests, and dust parameter exam have been conducted | Not done you lose time Build up of gas Bad roof |  |  |  |
| Ensure ventilation controls, signage and streamers are in place | Prevents accidental traveling under unsupported roof |  |  |  |
| Position yourself on left side of miner |  |  |  | Follow cut sequence diagram Easier to stay on sites See schematic Caution: Do not stand directly behind the conveyor of the miner – the conveyor chain can propel rock and coal at great speed and pressure |
| Hook the right bull wheel into the start mark |  |  |  | Foreman will measure back 16’ from center to get start mark |
| Slew the rear of miner around as much as possible toward the left rib |  |  |  |  |
| Mine the corner approximately 16’ |  |  |  | 60 degree crosscut Follow coal cutting procedures |
| After reaching the 16’ mark, back it up out of the corner |  |  |  |  |
| Mine left corner in about 10’ |  |  |  |  |
| Back up and reposition the miner to finish the right side cut |  |  |  |  |
| Cut coal until you hit the 40’ mark |  |  |  |  |
| Move to left side and repeat cut cycle |  |  |  |  |
| Clean up cut |  |  |  | Make two to three passes |
| Conduct gas test on left side with Gizmo | Not done you lose time Build up of gas |  |  | 20 minute intervals and at end of clean up |
| Clean scrubber according to plan |  |  |  |  |

# Duty 9:   Turn Crosscut to the Left

Learner will demonstrate how to safely turn left crosscuts (belt to L1 and R2) with the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls. Procedures for safely turning left crosscuts with the Joy 14CM RC Continuous Mining Machine with attached mobile bridge haulage include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| Ensure workplace exam, gas tests, and dust parameter exam have been conducted | Bad roof Gas Build up Not done you lose time |  |  |  |
| Ensure ventilation controls, signage and streamers are in place | Prevents accidental traveling under unsupported roof |  |  |  |
| Position yourself on right side of miner (inby) on the site line |  |  |  | Follow cut sequence diagram Do not stand directly in line with the cm conveyor chain - the chain can propel rock or coal with great velocity and force |
| Hook the left bull wheel into the start mark |  |  |  | Foreman will measure back 16’ from center to get start mark |
| Slew the rear of miner around as much as possible toward the right rib |  |  |  |  |
| Mine the corner in approximately 16’ |  |  |  | 60 degree crosscut Follow coal cutting procedures |
| After reaching 16’ mark, back it up out of the corner |  |  |  |  |
| Mine right corner in about 10’ |  |  |  |  |
| Slew miner around while taking corner and take right side in 40’ |  |  |  |  |
| Cut coal until you hit the 40’ mark |  |  |  |  |
| Move to left side and repeat cut cycle |  |  |  |  |
| Clean up |  |  |  | Make two to three passes |
| Conduct gas test with Gizmo | Not done you lose time Gas build up |  |  | 20 minute intervals and at end of clean up |
| Ensure scrubber has been cleaned according to plan |  |  |  |  |

# Duty 10:   Belt-up

Learner will demonstrate how to conduct a safe and thorough belt-up procedure using the Joy 14CM RC Continuous Mining Machine.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  A thorough belt-up move includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check travel way and work area conditions |  |  |  | Always examine work area and work place for hazards |
| Position miner outby RFM tail |  |  |  | About four feet outby A roll of belt will be spotted |
| Spot a splice at the tail |  |  |  |  |
| Use vice grips to hook roll of belt onto RFM belt |  |  |  | Outby splice RFM belt will unspool new belt |
| Turn on RFM belt |  |  |  |  |
| Run 100’ back |  |  |  |  |
| Shut belt off and lock out | Could cause serious injury if belt starts unexpectedly |  |  |  |
| Tram miner up past the tail |  |  |  |  |
| Place the frame of the miner against the RFM tail |  |  |  |  |
| Push the RFM back to obtain slack belt |  |  |  |  |
| Pull the spindle and hook the belt up |  |  |  |  |
| Attach pull chain to draw bar on miner |  |  |  |  |
| Pull RFM to next location with miner |  |  |  |  |
| Keep RFM on sites |  |  |  |  |
| Hook other end of the belt up |  |  |  |  |
| Install structure |  |  |  |  |
| Pull belt tight with miner |  |  |  |  |
| Energize the RFM belt |  |  |  |  |
| Start the RFM belt | Unexpected movement could cause injury to other workers |  |  | Communicate intentions to start belt to other crew members |
| Check for tracking |  |  |  |  |
| Follow signaling procedures when moving continuous miner or starting the RFM belt |  |  |  |  |
| Clean belt line |  |  |  |  |
| Reinstall belt back check |  |  |  |  |
| Advance CO monitor |  |  |  |  |
| Advance pull cord | You have to be able to shut belt off in case of an emergency |  |  |  |
| Advance water line |  |  |  |  |
| Vent belt air to return |  |  |  |  |
| Patch old return hole |  |  |  |  |

# Duty 11:   Normal End-of-Shift Activities (Hot-seating)

Learner will explain the importance of communicating and exchanging information as part of “hot seating (1st to 2nd shift) activities.  The learner will explain each job step, why they are conducted, any associated risk, and how to implement appropriate controls.  Hot seating activities include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Talk to oncoming operator | This discussion can point out potential hazards or road blocks to production on upcoming shift |  |  |  |
| Discuss problems with remote, shutdown switch, etc. | This discussion can point out potential hazards or road blocks to production on upcoming shift |  |  |  |
| Discuss time frame for gas tests, if necessary |  |  |  |  |
| Discuss roof conditions | This discussion can point out potential hazards or road blocks to production on upcoming shift |  |  |  |
| Discuss changes in bottom | This discussion can point out potential hazards or road blocks to production on upcoming shift |  |  | Soft, wet and broken up |
| Check travel way conditions on the way out |  |  |  | Always examine work area and work place for hazards |
| Drive mantrip out |  |  |  | Put on safety glasses before mantrip moves |
| Check out |  |  |  |  |
| Put methane detector on charge |  |  |  |  |
| Put light on charge |  |  |  |  |

# Duty 12:   End-of-Shift

Learner will demonstrate how to conduct safe and thorough end-of-shift (Saturday) activities.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and thorough end-of-shift (Saturday) activities include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Take only 20-foot cuts the 2nd half of shift | If 40’ is left standing could have build up of gas and could cause roof to sag |  |  |  |
| Check travel way and work area conditions |  |  |  | Always examine work area and work place for hazards |
| Back miner up along RFM |  |  |  |  |
| Shut belt off | Could be a fire hazard Belt being left on could cause problem on start-up next production shift Belts could start unexpectedly |  |  |  |
| Check ventilation | Excessive gas build up over the weekend |  |  |  |
| Make sure proper danger signs are posted | Everyone is aware of all dangers |  |  |  |
| Shut water off at Christmas tree |  |  |  |  |
| De-energize all equipment at power center | Fire hazard Ignition source if left unattended |  |  |  |
| Contact outside that your are done loading |  |  |  |  |
| Drive man trip out |  |  |  | Put on safety glasses before mantrip moves |
| Check out |  |  |  |  |
| Put methane detector on charge |  |  |  |  |
| Put light on charge |  |  |  |  |

# Duty 13:   Remote Box Functions

Learner will demonstrate how to safely operate the Joy 14CM RC Continuous Mining Machine remote box in a non-production setting. Learner will also explain the controls, what they operate and how they function.  Using the remote box includes the following:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Stay in sight of machine at all times while testing or using the box | Miner can move with remote box functions even though it is out of sight |  |  | Give trainee adequate time to learn and practice these controls Have control diagram/drawing or practice box available for use in training |
| Demonstrate panic bar | Written in Blood |  |  | Push or pull will shut the machine down |
| Demonstrate emergency stop (E-stop) | Back-up Fail safe/ shut down |  |  | Kicks power to the load center |
| Demonstrate installation of battery to remote box |  |  |  |  |
| Start the pump motor |  |  |  |  |
| Leave it in the pump cycle mode |  |  |  |  |
| Demonstrate head function |  |  |  | Up and down |
| Demonstrate pan function |  |  |  | Up and down |
| Demonstrate tail function |  |  |  | Up and down |
| Demonstrate stab jack function |  |  |  | Up and down |
| Demonstrate fire suppression |  |  |  | Turn it on with remote |
| Demonstrate how to shut off fire suppression manually after being activated |  |  |  | Turn it off at the miner |
| Demonstrate function of water sprays |  |  |  |  |
| Demonstrate how to turn head lights off and on |  |  |  |  |
| Demonstrate override of on-board panic buttons |  |  |  | Panic buttons located on each side of machine - explain reasons for use |
| Demonstrate tram speed switch |  |  |  | Low and high tram |
| Demonstrate tram levers function |  |  |  | Forward, backward, left and right |
| Demonstrate coal chain activation |  |  |  |  |
| Demonstrate activating scrubber |  |  |  |  |
| Demonstrate cutter head start procedure |  |  |  | Trainee should be given a period to practice Power off practice initially |

# Duty 14:  Using the Gizmo

Learner will demonstrate how to correctly operate the Gizmo. Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Proper procedures for correctly operating the Gizmo will include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Shut machine down using panic switch on remote | Cutter heads have been known to start accidentally Could cause crushing injuries. |  |  | Accidental activation of remote box has caused serious injuries -always shut machine down when working in close proximity |
| Check work area conditions |  |  |  | Always examine work area and work place for hazards |
| Place Gizmo no further than 30” outby the tip of the bits on the right side gear case | If it is on any further than 30” may not detect full gas concentration |  |  |  |
| Activate methane detector | Won’t work if you don’t turn it on, could waste time having to tram machine the second time |  |  |  |
| Signal bridge crew |  |  |  |  |
| Tram miner to face | You need to get to where the bits hit the solid coal to get a good reading |  |  | Deepest penetration Observe Gizmo as your are tramming to ensure that it stays in place |
| Touch bits to face | You need to get to where the bits hit the solid coal to get a good reading |  |  |  |
| Observe reading | You need to know if there is any gas in the face |  |  |  |
| Take a time check | To notify the bolter, if not bolter has to use the 40’ probe |  |  |  |
| Flag the bridge man and back out |  |  |  |  |
| Tell roof bolter operators time of gas test | To notify the bolter, so the bolter will know when his 20 minutes is up and he has to take another check |  |  |  |

# Duty 15: Installing sight lines

Learner will demonstrate how to safely and efficiently install sight lines.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Safe and efficient installation of sight lines includes the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Check travel way and work area conditions |  |  |  | Always examine work area and work place for hazards |
| Find laser |  |  |  | You can use other instruments to take sites |
| Find spads |  |  |  |  |
| Hang laser |  |  |  |  |
| Paint center line from face to 20’ outby following laser beam | Being off site can cause extra work Being off site could prevent you from making proper air connections and could affect roof control |  |  | Do not look into laser beam |

# Duty 16:   Non-Routine Tasks/Unusual Activities

Learner will discuss, explain and demonstrate when necessary, proper procedures for dealing with non-routine tasks or unusual or emergency situations associated with the operation of the Joy 114CM RC Continuous Mining Machine with attached mobile bridge haulage.  Learner will also explain the job duties, why they are conducted, any associated risk, and how to implement appropriate controls.  Procedures for dealing with non-routine tasks, unusual or emergency situations include the following job steps:

| Job Steps | Importance Narrative (Consider Safety, Production, Maintenance) | Importance Ranking 1=Important 2=Very Important 3=Critical | Satisfactory or Needs Work | Procedures/Risk Resolution/ Notes/Comments |
| --- | --- | --- | --- | --- |
| Explain fire-fighting duties | Every person assignment is critical in the event of a fire |  |  | Assist foreman with ventilation |
| Show location of manual fire valves | In case there is a fire it is imperative to know where they are at and how to turn them on |  |  | One each on left and right sides of miner and one back 40’ on bridge |
| Show escapeways | Everyone is responsible to know their escapeways and evacuation procedures |  |  |  |
| Explain/demonstrate methane monitor signals (MMS) and display | In case of methane accumulation it is important to understand what your signals mean |  |  |  |
| Explain display |  |  |  | Display shows methane in tenths of a percent Flashes at 1.0% Shuts machine off a 2.0% |
| Explain signals | In case of methane accumulation it is important to understand what your signals mean |  |  | Red signals on each side Shines solid with power on Flashes at 1.0% Kicks power at miner at 2.0% |
| Explain procedures to follow when methane approaches 1.0% | By following this procedure you can prevent accumulations of methane and continue loading without disrupting the mining cycle |  |  | Slow cutting down Back away from face Resume normal cutting when percentage lowers |
| Explain procedures to follow when 1.0% methane is detected | By following this procedure you can prevent explosive accumulations Eliminates ignition source when methane is detected |  |  | Stop cutting Back machine away from face Make adjustments to ventilation De-energize miner If methane reading remains 1.0% or greater, test for gas with handheld detector |
| Explain procedures to follow when 2.0% methane is detected | By following this procedure you can prevent explosive accumulations Eliminates ignition source when methane is detected |  |  | Machine will shut off automatically |
| Make official methane examination | By following this procedure you can determine/verify the degree of danger |  |  | Use probe and handheld methane detector |
| 2.0% or over is detected | By following this procedure you can determine/verify the degree of danger and course of action |  |  | Report to foreman All personnel except those needed to ventilate the methane should be removed from the area Foreman is required to re-examine all faces for gas |
| Remove power from all equipment | Eliminates ignition sources |  |  | At load center |
| Explain procedures to follow when machine breaks down inby permanent support | Roof falls are the Number 1 Killer of coal miners |  |  | Review applicable portion of the roof control plan |
| Explain mining procedures to follow when bad roof is encountered | Roof falls are the Number 1 Killer of coal miners Roof conditions are a judgment call, if in doubt discuss with foreman and bolters |  |  | No deep cuts Narrow the lift up Cut down loose rock Make roof bolters aware of roof conditions |
| Using probes |  |  |  |  |
| Obtain probe |  |  |  | Usually on bolter or by phone 20” and 40” probes available |
| Stay under supported roof | Roof falls are the Number 1 Killer of coal miners Loss of employment |  |  |  |
| Put legs on end of probe |  |  |  | 40’ probe only |
| Extend probe and slide to face |  |  |  | To deepest penetration You may need to maneuver over the miner |
| Take methane reading |  |  |  |  |
| Retract probe |  |  |  |  |
| Replace probe |  |  |  |  |
| Procedures for crossing over/under bridges | There have been serious injuries and fatalities when crossing moving conveyor systems/bridges |  |  | Never cross over or under a bridge until the bridges are on the bottom and shut down. |