United States Department of Agriculture

Indiana - February 2008 (ver. 1.0)

Native Grass Plantings Program Job Sheet

purpose

Native grass plantings are used to reduce soil erosion, improve water quality, and create or enhance wildlife habitat.

Native grass communities are often associated with prairies, barrens, and savannas.  Common native grasses that grow well in Indiana include warm-season grasses (WSG) such as Big Bluestem, Little Bluestem, and Indiangrass, as well as native cool season grasses such as Canada Wild Rye and Virginia Wild Rye.  Native grass communities also included common wildflowers (forbs) such as Black-Eyed Susan, Purple Coneflower, Prairie Blazing Star, and others.

Native grass plantings of warm-season species provide excellent nesting and winter cover for wildlife.  These tall, stiff, upright grasses stand up well to snow and ice.  Native grasses grow mostly in the heat of the summer, unlike the cool-season grasses (found in most lawns) which grow best in the spring and fall.

Native grasses persist long after establishment.  However, like most long-lived plant species, they generally establish slowly.  Therefore, it is very important to establish these grasses properly and to have patience when evaluating the results.

Where Practice Applies

On fields that meet eligibility requirements for the Conservation Reserve Enhancement Program (CREP) as determined by the Farm Service Agency (FSA).

CREP Policy

The grass planting will consist of at least three (3) native grass species, plus at least two (2) forbs or legumes.

CREP Native Grass Plantings are only eligible on cropland that is adjacent and parallel to streams, sinkholes and karst areas, wetlands, and permanent bodies of water such as lakes/ponds.

The minimum width of CREP Native Grass Plantings will be a minimum of 50 feet, and a maximum of 120 feet, from the edge of the eligible body of water.  NOTE:  An average maximum width of 300 feet is allowed when area to be enrolled involves a predominance of alluvial soils.  If the site already contains existing vegetation, these acres will be included in the calculation of maximum width and included in the CREP Plan, but will not be eligible for payments.

Seeding Rates and Species

Seeding rates for native grasses and legumes/forbs are found in the Upland Wildlife Habitat Management (645) Standard of the Natural Resources Conservation Service (NRCS) electronic Field Office Technical Guide (eFOTG).  Any pre-packaged mixes must be approved before seeding.  Site-specific requirements are listed on the attached Specifications Sheet.

PLANTING

Plant the vegetation according to the attached plan/design sheet.  Any changes to these specifications should be approved by NRCS.  All construction and seeding must be completed within 12 months of contract approval to remain in compliance.  If circumstances beyond the landowner’s control prohibit completion within the first 12 months, the local FSA County Committee may approve an extension to the next construction and planting season.

Site Preparation:  It is very important to plant the vegetation into a weed-free seedbed.  Weed control efforts should begin prior to planting, and may require multiple applications in both the fall and spring prior to planting.  Use herbicides or tillage to eliminate competing vegetation.  If necessary for erosion control, seed a temporary cover.  Eliminate the temporary vegetation at planting time with tillage or herbicides.

Contact your local Purdue University Extension Agent for specific herbicides to use.  Apply all herbicides according to the label.

Lime and Fertilizer:  Lime and fertilizer should not be applied to native grasses at establishment unless a current soil test shows phosphorus (P) and potassium (K) are in the deficient range or the pH is 6.1 or less.  Do not apply any nitrogen (N) during establishment to minimize weed competition.

Seeding Dates:

| Species/Mix | IN Seeding Dates | Dormant Seeding Dates* |
| --- | --- | --- |
| Warm Season Grasses | 4/1-6/15 | 12/1-4/1 |
| Legumes | 3/1-5/15 or 8/1-9/15 | 12/1-3/1 |
| Forbs | 4/1-6/15 | 12/1-4/1 |

*Increase seeding rates by 25% dormant seeding.  Broadcasting of warm season grasses should only be done into a prepared seedbed with protection from erosion as a consideration.

Seed preparation:  Inoculate legume seed before seeding with the proper Rhizobia bacteria specific for the species.  Re-inoculate seed if it was pre-inoculated more than 60 days prior to seeding.  Be careful not to blend seed of varying size, shape and weight as this can make calibration of equipment and seeding uniformity difficult.

No-Till seeding: Use a no-till drill to reduce the risk of erosion and possible loss of seedlings.  Ensure the drill is designed to handle the seed being planted (especially important for native grasses).  Your local Soil and Water Conservation Districts may be able to assist in locating equipment.  Set the drill to provide an ideal planting depth of no more than ¼ inch unless otherwise directed.  Seeding native grasses deeper than ¼ inch will lead to potential failure.  Soils that are too wet or too dry can also cause improper seed placement.

Conventional Seeding:  Use a drill with seven (7) inches or less row spacing or a culti-packer seeder, designed for the seed to be planted.  The seedbed should be worked to a minimum depth of three (3) inches and firmed before seeding.  Grass seed should be drilled uniformly and seeded no more than 1/2 inch deep.

Broadcast Seeding:  Seed may be broadcast if completed in a uniform manner.  Pre-mixing the seed with 200 lbs. per acre of pelletized lime and utilizing an airflow applicator is also effective.  Seedbeds should be worked to a minimum depth of three (3) inches and firmed before seeding.  The seedbed should be culti-packed before and after seeding.  It is acceptable to see up to ⅓ of the seed on the soil surface.  Wind speed should be 15 m.p.h. or less when broadcasting.

Weed Control During Establishment Period: Mow, burn, or apply herbicides as needed to control unwanted vegetation until a Final Status Review is issued, or for a maximum of 3 years after planting.  Mow when competing weeds are taller than the planted vegetation, and at a height above planted vegetation.

OPERATION AND MAINTENANCE

Noxious weeds and other undesirable plants, insects, and pests shall be controlled, including such maintenance as necessary to avoid detrimental effects to the surrounding land.

After the Final Status Review or three (3) years (whichever comes first), maintain the planting according to your CREP conservation plan.  Maintenance activities are allowed only on a spot basis and only if necessary to maintain stand health, maintain stand diversity, or control pests that will damage the CREP cover or adjacent lands.  Burning must be in accordance with a prescribed burn plan.  MOWING and other maintenance activities are not authorized between April 1 to August 1 to protect ground-nesting wildlife (i.e. - the Primary Nesting and Brood-Rearing season).  If maintenance activities are needed during these times, the FSA County Committee must approve the maintenance activity prior to the activity occurring.  Native grasses will not be mowed lower than 12 inches.  Mowing for generic weed control or for cosmetic purposes is prohibited.  Livestock must be excluded from the CREP Native Grass Plantings.

MID-CONTRACT  MANAGEMENT

All CREP contracts must have mid-term contract management activities scheduled that will ensure plant diversity, wildlife habitat, and protection of soil and water resources.  Management activities that will ensure these benefits include: prescribed burning (according to an approved burn plan), strip disking, strip spraying, and inter-seeding of forbs and legumes.  All management activities must be performed according to NRCS Standards and Specifications as found in the eFOTG, and CREP policy.  Mid-management job sheets can be found at the NRCS CRP web site.

Managed Haying and Grazing

These plantings may be used for managed haying or grazing.  These activities must be performed according to NRCS Standards and Specifications as found in the FOTG and CREP policy.  The same acreage may not be hayed or grazed more than once every 3 years.  Annual CREP rental payments will be reduced based on the value of the forage removed.  All managed haying and grazing activities must be conducted outside of the primary nesting season (April 1 to August 1) and must be approved by FSA and included in the conservation plan prior to harvesting the forage.

CREP Native Grasses Planting (CP-2) SPECIFICATIONS SHEET

| Landowner: | County: |
| --- | --- |
| Farm: | Tract: | Field(s): | Acres: | Grass/Legume Mix #1: Grass/Legume Mix #2: Firebreak: | Date: |

| Recommended Species and Seeding Rates |
| --- |
| Use the Seeding Mixture Calculator in the NRCS Upland Wildlife Habitat Management Standard (645) for seeding rates. All rates are in Pure Live Seed (PLS) |
|  | Grass/Legume mix #1 | Rate Lb./acre | Total = (Rate X Acres) |  | Grass/Legume mix #2 | Rate Lb./acre | Total = (Rate X Acres) |
|  |  |  | 0.00 | Lb. |  |  |  | 0.00 | Lb. |
|  |  |  | 0.00 | Lb. |  |  |  | 0.00 | Lb. |
|  |  |  | 0.00 | Lb. |  |  |  | 0.00 | Lb. |
|  |  |  | 0.00 | Lb. |  |  |  | 0.00 | Lb. |
|  |  |  | 0.00 | Lb. |  |  |  | 0.00 | Lb. |
|  | Additional Forbs | Rate Oz./acre | Total = (Rate X Acres) |  | Additional Forbs | Rate Oz./acre | Total = (Rate X Acres) |
|  |  |  | 0.0 | Oz. |  |  |  | 0.0 | Oz. |
|  |  |  | 0.0 | Oz. |  |  |  | 0.0 | Oz. |
|  |  |  | 0.0 | Oz. |  |  |  | 0.0 | Oz. |
|  |  |  | 0.0 | Oz. |  |  |  | 0.0 | Oz. |
|  |  |  | 0.0 | Oz. |  |  |  | 0.0 | Oz. |
|  |  |  | 0.0 | Oz. |  |  |  | 0.0 | Oz. |
| Firebreaks: | Species/Activity | Rate Lb./acre | Total = (Rate X Acres) |
|  |  |  | 0.00 | Lbs. |
|  |  |  | 0.00 | Lbs. |
|  | Establish a Bare-Ground Firebreak by disking the Fall & Spring prior to Prescribed Burning Disked areas will be re-seeded after each Prescribed Burn |
| NOTES: |

| Site Preparation - BEFORE Planting in Year: |
| --- |
| Herbicide (per label): |  | Dates: |
| Herbicide (per label): |  | Dates: |
| Herbicide (per label): |  | Dates: |
| Tillage: |  |
| Prescribed Burning: |  |
| Temporary Seeding: |  |
| Other: |  |
| NOTES: |

| Planting Year: |
| --- |
| Planting Method (grass planting): |  | Date: |
| Planting Method (firebreak): |  | Date: |
| If unforeseen circumstances prohibit planting by this date, please contact the local NRCS office as soon as possible. |

| Post-Planting Maintenance |
| --- |
| Mowing: BEFORE final Status Review, or up to three (3) years, mow to a minimum height of six (6) to eight (8) inches high when the weeds are 12 inches taller than the planted grasses |
| *AFTER final Status Review, or up to three (3) years, mow to a minimum height of six (6) to eight (8) inches |
| Herbicide* (per label): |  | Prescribed Burning*: According to an approved plan |
| Other: |
| *NOTE: After the final Status Review has been issued, or three (3) years (whichever comes first), weed control and other maintenance activities will be conducted outside the nesting season of April 1 - August 1, and on a “spot” basis only, unless prior approval is granted by the FSA County Committee. |

Mid-Contract Management Starting In Year:

Prescribed Burning: according to an approved burn plan Burning will not occur more than once every 3 years on the same acreage.

Strip Spraying: Spraying will not occur more than once every 3 years on the same acreage.

Strip Disking: Disking will not occur more than once every 3 years on the same acreage.

Inter-seeding: Inter-seeding will not occur more than once every 3 years on the same acreage.

The Specific Mid Contract Management Activity will be decided by the participant in the scheduled year based on condition of the vegetation, site considerations, capabilities of the participant, etc. Treatment will not occur more than once every 3 years on the same acreage. Reimbursement will be dependant on the activity(s) performed based on local FSA Not-To-Exceed rates.

1 See NRCS CRP Mid-contract Management job sheets for additional information.

Additional Information

Helping People Help the Land

USDA is an equal opportunity provider and employer

# Text boxes

CREP

Practice CP2