Mr. John Giusti

Acting Chief of the International Bureau

Federal Communications Commission

445 12th Street SW

Washington, D.C. 20554

Dear Mr. Giusti:

The National Telecommunications and Information Administration (NTIA), on behalf of the Executive Branch Agencies, adopted the attached proposal as a replacement for the proposal on Agenda Item 1.20 transmitted to the Commission on March 17, 2006.  The revised proposal responds to comments by the FCC WRC Advisory Committee (WAC) on the earlier Executive Branch proposal.

The replacement proposal includes the following additional points: (1) adopts the WAC-suggestion that the limits should be brought into use after the last day of WRC-07;  (2) adds to each footnote that the ITU Radiocommunication Bureau "shall make neither examination nor finding" in response to a second IWG-1 comment;  (3) relaxes the unwanted emission limit on 50 GHz FSS uplinks by 13 dB based on further analysis and discussions with satellite industry representatives;  (4) adds a separate unwanted emissions limit, relaxing the maximum limit by 6 dB during rain fading events, for 50 GHz FSS uplinks in response to the WAC proposal and discussions with industry;  (5) corrects the band limit inconsistencies pointed-out by the WAC; and (6) addresses the impact to active services in response to the IWG-1 comment that it was premature to make assertions about the impact on active services.

It is important that the necessary unwanted emission limits be imposed now so that the passive service in certain critical bands will be protected as active services are introduced into the adjacent bands.  So far there has been no specific information brought forth by the active services that the new unwanted emissions limits would be overly burdensome to their operations.

This proposal is forwarded for your earliest consideration.  Jim Vorhies of my staff is the primary contact for NTIA.

# Sincerely,

(Original Signed October 20, 2006)

# Fredrick R. Wentland

Associate Administrator

Office of Spectrum Management

Enclosure

United States of America

## DRAFT PROPOSAL FOR THE WORK OF THE CONFERENCE

WRC-07 Agenda Item 1.20:  to consider the results of studies, and proposals for regulatory measures, if appropriate, regarding the protection of the Earth exploration-satellite service (passive) from unwanted emissions of active services in accordance with Resolution 738 (WRC–03);

Background Information:  The resolves in Resolution 738 calls for three actions: 1) study the compatibility between EESS (passive) and the corresponding active services listed in the Table in Resolution 738 to update Recommendation ITU-R SM.1633 or develop additional Recommendations; 2) further study the impact of implementing the values in considering f ) and g) in the bands 31–31.3 GHz and 51.4–52.6 GHz for unwanted emissions of systems operating in Region 2 and 3, taking into account that the impact on fixed-service systems in Region 1 is documented in ITU-R Recommendation SM.1633; and 3) review the results of studies in 1) and 2) in order to consider regulatory measures, if appropriate, to ensure the protection of the EESS (passive) operating in the bands listed in the table in Resolution 738 (WRC 03) from unwanted emissions of active services operating in the corresponding bands while taking into account the impact on all concerned services of implementing or not implementing such measures. The table below shows the frequency band and radiocommunication service combinations within the scope of the agenda item.

| EESS (passive) band | Active service band | Active service |
| --- | --- | --- |
| 1 400-1 427 MHz | 1 350-1 400 MHz | Fixed service (FS) Mobile service (MS) Radiolocation service (RLS) |
|  | 1 427-1 429 MHz | FS, MS (except aeronautical mobile service (AMS)) and space operation service (Earth-to-space)1 |
|  | 1 429-1 452 MHz | FS and MS |
| 23.6-24 GHz | 22.55-23.55 GHz | Inter-satellite service (ISS) |
| 31.3-31.5 GHz | 30-31 GHz | FSS (Earth-to-space) |
|  | 31-31.3 GHz | FS (except HAPS) |
| 50.2-50.4 GHz2 | 50.4-51.4 GHz2 | FSS (Earth-to-space)2 |
|  | 47.2-50.2 GHz (Regions 2 and 3) 49.44-50.2 GHz2 (Region 1) | FSS2 |
| 52.6-54.25 GHz | 51.4-52.6 GHz | FS |
| 1 Resolution 738 (WRC 03) incorrectly refers to the space research service instead of the space operation service. 2 Studies in this band must take into account No. 5.340.1. |

Studies documented in Recommendation ITU–R SM.1633 show that active services in some of these bands do not produce significant unwanted emissions in the adjacent passive band. However, active services in other bands produce unwanted emissions in excess of EESS (passive) protection requirements.  Because of the differences between the active services, and the differences in the use of the active and passive services from band to band, the solutions for this agenda item have been determined on a band-by-band and service-by-service basis.

Regulatory certainty is achieved for the most problematic cases (6 of the 13 cases where bands and services were identified for consideration in Resolution 738) by administrations limiting unwanted emissions for cases where interference is likely to occur without some action being taken.  This is accomplished by RR provisions that apply to administrations operating systems in these six band/services.  Administrations would then need to apply those limits in their operations in order to be in compliance with their ITU treaty obligations.  A non-mandatory limit published by the ITU would provide useful guidance to administrations but would not provide any level of certainty.  While the imposition of the limits will not guarantee that the performance of the passive satellite networks will be unimpaired as new active service transmitters in nearby bands are implemented, the Administration-imposed limits will provide some certainty that the worst interfering cases will be avoided.  Second, at this stage of implementation of active services in many of the nearby bands, the emission limits are part of the design considerations from the start rather than retrofitting or modifying existing equipment designs.

The proposals do not require, and no provision is made for, ITU Radiocommunication Bureau examination, or enforcement of these limits.

Resolution 738 can be suppressed, and there is no need for an agenda item dealing with unwanted emission levels in EESS (passive) bands for the next Conference.

Proposal:

USA/  /1	MOD

| 1 300-1 525 MHz |
| --- |
| Allocation to services |
| Region 1 | Region 2 | Region 3 |
| …… |
| 1 350-1 400 FIXED ADD 5.AAA MOBILE RADIOLOCATION | 1 350-1 400 RADIOLOCATION |
| 5.149 5.338 5.339 5.339A | 5.149 5.334 5.339 5.339A |
| 1 400-1 427 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 5.341 |
| 1 427-1 429 SPACE OPERATION (Earth-to-space) ADD 5.BBB FIXED ADD 5.AAA MOBILE except aeronautical mobile 5.341 |
| 1 429-1 452 FIXED ADD 5.AAA MOBILE except aeronautical mobile | 1 429-1 452 FIXED ADD 5.AAA MOBILE 5.343 |
| 5.339A 5.341 5.342 | 5.339A 5.341 |
| …….. |

USA/  /2	ADD

5.AAA		In order to ensure the protection of the Earth exploration-satellite (passive) service in the band 1 400–1 427 MHz, the unwanted emissions power in the 1 400–1 427 MHz band delivered to the antenna of any station in the fixed service operating in the band 1 350–1 400 MHz or in the band 1 427–1 452 MHz shall not exceed –45 dBW/27 MHz.  This provision shall apply only to fixed service stations brought into use after 9 November 2007. The Bureau shall make neither examination nor finding with respect to this provision under either Article 9 or 11.

Reasons:  Results of studies documented in Recommendation ITU–R SM.1633 show that large numbers of higher power fixed service transmitters can cause significant levels of unwanted emissions in the 1 400–1 427 MHz passive band.  The single-entry unwanted emission limit proposed for future systems will slightly exceed the desired protection level of the EESS (passive) sensors in some cases, but will still allow the collection of valuable scientific data.

USA/  /3	NOC

No change to Radio Regulations regarding the radiolocation service allocation in the band 1 350–1 400 MHz.

Reasons: Although studies documented in Recommendation ITU–R SM.1633 show that the radiolocation unwanted emissions in the EESS (passive) band at 1 400–1 427 MHz would exceed the permissible interference threshold in Recommendation ITU–R SA.1029–2, any interference would occur for only short time periods and would be readily discernible by users of the remote sensing data, allowing corrupted data to be discarded. The remaining uncorrupted data is expected to satisfy the scientific objectives of the EESS missions. Studies also show that radars would experience unacceptable degradation in operational coverage and range, target resolution, and accuracy if required to meet unwanted emission limits in the 1 400–1 427 MHz band.  As with other pairs of active and passive bands, use of portions of the allocated bands must not be restricted.  Radars would suffer an increased likelihood of interference from other radars and a reduction in coverage range, while a reduced bandwidth would be inadequate for remote sensing requirements.

USA/  /4	ADD

5.BBB		In order to ensure the protection of the Earth exploration-satellite (passive) service in the band 1 400–1 427 MHz, the unwanted emissions e.i.r.p. in the 1 400–1 427 MHz band of any earth station in the space operation service (Earth-to-space) operating in the band 1 427–1 429 MHz shall not exceed 8 dBW/27 MHz.  This provision shall apply only to space operation service earth stations brought into use after 9 November 2007 The Bureau shall make neither examination nor finding with respect to this provision under either Article 9 or 11.

Reasons:  Results of studies documented in Recommendation ITU–R SM.1633 show that earth station transmitters in the 1 427–1 429 MHz band can cause significant levels of unwanted emissions in the 1 400–1 427 MHz passive band. The single-entry unwanted emission limit proposed for future systems will slightly exceed the desired protection level of the EESS (passive) sensors in some cases, but will still allow the collection of valuable scientific data.

| 22-24.75 GHz |
| --- |
| Allocation to services |
| Region 1 | Region 2 | Region 3 |
| …. |
| 22.55-23.55 FIXED INTER-SATELLITE MOBILE 5.149 |
| 23.55-23.6 FIXED MOBILE |
| 23.6-24 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 |
| …. |

USA/  /5	NOC

No change to Radio Regulations regarding the inter-satellite service allocation in the band 22.55–23.55 GHz.

Reasons:  Results of studies documented in Recommendation ITU–R SM.1633 show that unwanted emissions from the ISS in the 22.55–23.55 GHz band are well below the recommended protection criteria for the EESS (passive) in the 23.6–24.0 GHz band.  Therefore, no changes are needed to the Radio Regulations to protect the EESS (passive) in the 23.6–24.0 GHz band from unwanted emissions from the ISS in the 22.55–23.55 GHz band.

USA/  /6	MOD

| 29.9-34.2 GHz |
| --- |
| Allocation to services |
| Region 1 | Region 2 | Region 3 |
| …. |
| 30-31 FIXED-SATELLITE (Earth-to-space) MOBILE-SATELLITE (Earth-to-space) Standard frequency and time signal-satellite (space-to-Earth) 5.542 |
| 31-31.3 FIXED 5.543A ADD 5.CCC MOBILE Standard frequency and time signal-satellite (space-to-Earth) Space research 5.544 5.545 5.149 |
| 31.3-31.5 EARTH EXPLORATION-SATELLITE (passive) RADIO ASTRONOMY SPACE RESEARCH (passive) 5.340 |
| …. |

USA/  /7	NOC

No change to Radio Regulations regarding the fixed-satellite service (Earth-to-space) allocation in the band 30-31 GHz.

Reasons:  Results of studies documented in Recommendation ITU–R SM.1633 show that unwanted emissions from the FSS in the 30-31 GHz band do not exceed the recommended protection criteria for the EESS (passive) in the 31.3-31.5 GHz band.  The FSS allocation is separated from the EESS (passive) allocation by 300 MHz, which greatly reduces the possibility of FSS unwanted emissions exceeding the protection criteria in the EESS (passive) band. Unwanted emission limits in the EESS (passive) band are unnecessary, and could constrain the future development of FSS uplink transmitters in the 30-31 GHz band.

USA/  /8	ADD

5.CCC		In order to ensure the protection of the Earth exploration-satellite (passive) service in the band 31.3–31.5 GHz, the unwanted emissions power in the 31.3–31.5 GHz band delivered to the antenna of any station in the fixed service operating in the band 31.0–31.3 GHz shall not exceed –38 dBW/100 MHz (see also No. 5.543A). This provision shall apply only to fixed service stations brought into use after 9 November 2007. The Bureau shall make neither examination nor finding with respect to this provision under either Article 9 or 11.

Reasons:  Studies documented in Recommendation ITU–R SM.1633 indicate that EESS (passive) systems in the 31.3–31.5 GHz band are protected if unwanted emissions in that band from fixed service transmitters in the 31.0–31.3 GHz band do not exceed –38 dBW in any 100 MHz reference bandwidth. Measures to ensure that future FS systems in the 31.0–31.3 GHz band do not exceed this level will not constitute an undue burden on the fixed service.

USA/  /9	MOD

| 40-47.5 GHz |
| --- |
| Allocation to services |
| Region 1 | Region 2 | Region 3 |
| …. |
| 47.2-47.5 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD MOBILE 5.552A |

47.5-51.4 GHz

| Allocation to services |
| --- |
| Region 1 | Region 2 | Region 3 |
| 47.5-47.9 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD (space-to-Earth) 5.516B 5.554A MOBILE | 47.5-47.9 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD MOBILE |
| 47.9-48.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD MOBILE 5.552A |
| 48.2-48.54 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD (space-to-Earth) 5.516B 5.554A 5.555B MOBILE | 48.2-50.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.516B 5.552 ADD 5.DDD MOBILE |
| 48.54-49.44 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD MOBILE 5.149 5.340 5.555 |  |
| 49.44-50.2 FIXED FIXED-SATELLITE (Earth-to-space) 5.552 ADD 5.DDD (space-to-Earth) 5.516B 5.554A 5.555B MOBILE | 5.149 5.340 5.555 |
| 50.2-50.4 EARTH EXPLORATION-SATELLITE (passive) SPACE RESEARCH (passive) 5.340 |
| 50.4-51.4 FIXED FIXED-SATELLITE (Earth-to-space) ADD 5.DDD MOBILE Mobile-satellite (Earth-to-space) |

USA/  /10	ADD

5.DDD		In order to ensure the protection of the Earth exploration-satellite (passive) service in the band 50.2-50.4 GHz, the unwanted emissions e.i.r.p. in the 50.2-50.4 GHz band of any earth station in the fixed-satellite service operating either in the band 47.2-50.2 GHz or in the band 50.4-51.4 GHz shall not exceed 43 dBW/200 MHz under clear sky conditions, or 49 dBW/200 MHz under fading conditions.  This provision shall apply only to fixed-satellite service earth stations brought into use after 9 November 2007. The Bureau shall make neither examination nor finding with respect to this provision under either Article 9 or 11.

Reasons:  Results of studies documented in Recommendation ITU–R SM.1633 show that fixed-satellite service uplink transmitters operating in bands adjacent to then 50.2-50.4 GHz passive band can cause significant levels of unwanted emissions in the 50.2-50.4 GHz passive band.

USA/  /11	MOD

| 51.4-55.78 GHz |
| --- |
| Allocation to services |
| Region 1 | Region 2 | Region 3 |
| 51.4-52.6 FIXED ADD 5.EEE MOBILE 5.547 5.556 |
| 52.6-54.25 EARTH EXPLORATION-SATELLITE (passive) SPACE RESEARCH (passive) 5.340 5.556 |
| …. |

USA/  /12	ADD

5.EEE		In order to ensure the protection of the Earth exploration-satellite (passive) service in the band 52.6–54.25 GHz, the unwanted emissions power in the 52.6–54.25 GHz band delivered to the antenna of any station in the fixed service operating in the band 51.4–52.6 GHz shall not exceed –33 dBW/100 MHz. This provision shall apply only to fixed service stations brought into use after 9 November 2007. The Bureau shall make neither examination nor finding with respect to this provision under either Article 9 or 11.

Reasons:  Studies documented in Recommendation ITU–R SM.1633 indicate that EESS (passive) systems in the 52.6–54.25 GHz band are protected if unwanted emissions in that band from fixed service transmitters in the 51.4–52.6 GHz band do not exceed –33 dBW in any 100 MHz reference bandwidth. Measures to ensure that future FS systems in the 51.4–52.6 GHz band do not exceed this level will not constitute an undue burden on the fixed service.

USA/  /13	SUP

RESOLUTION  738  (WRC-03)

Compatibility analyses between the Earth exploration-satellite 
service (passive) and active services

Reasons:  Consequential to completion of this agenda item.  All of the actions required under this Resolution will have been completed at WRC-07 and it may be suppressed.  The technical studies will either have confirmed that the unwanted emissions do not interfere with the EESS (passive) or appropriate regulatory measures, if necessary, will have been determined and decided by WRC-07.

# Footnotes

The initial unwanted emission EIRP limit was based on a "worst case" deployment scenario in Asia.  The revised value is based on a more average deployment scenario as would be typical for example in Europe.

This is a second version of the Executive Branch proposal (October 2006)

Protection values are contained in Resolution 738 considering f and g as follows :  f)	that according to Recommendation ITU-R SM.1633, the EESS (passive) in the band 31.3-31.5 GHz can be protected if the unwanted emissions of fixed-service systems (except high-altitude platform stations (HAPS)) operating in the band 31.0-31.3 GHz do not exceed –38 dBW in a 100 MHz reference bandwidth in the band 31.3-31.5 GHz;

g)	that according to Recommendation ITU-R SM.1633, the EESS (passive) in the band 52.6-54.25 GHz can be protected if the unwanted emissions of fixed-service systems operating in the band 51.4-52.6 GHz do not exceed –33 dBW in a 100 MHz reference bandwidth in the band 52.6-54.25 GHz;

Administrations generally adhere to their treaty obligations whether there is ITU enforcement or not.  Regulators have understandably stated that provisions in the RR allowing a finding by the ITU of harmful interference to passive satellite service from unwanted emissions would be unworkable and unwise.