SPECIAL SPECIFICATION

SECTION 10655

ACCORDION FOLDING PARTITIONS

Page

PART 1 - GENERAL

1.01	Related Documents ..............................................................................	2

1.02	References ........................................................................................	2

1.03	Summary .........................................................................................	2

1.04	Submittals ........................................................................................	3

1.05	System Performance Requirements ...........................................................	3

1.06	Quality Assurance ...............................................................................	4

1.07	Delivery, Storage and Handling ...............................................................	4

PART 2 - PRODUCTS

2.01	Manufacturers ....................................................................................	4

2.02	Suspension Systems.............................................................................	5

2.03	Posts and Seals ..................................................................................	5

2.04	Finish Surface ...................................................................................	5

2.05	Hardware .........................................................................................	5

PART 3 - EXECUTION

3.01	Examination .....................................................................................	6

3.02	Installation .......................................................................................	6

3.03	Adjusting ........................................................................................	6

3.04	Cleaning .........................................................................................	6

SPECIAL SPECIFICATION

SECTION 10655

ACCORDION FOLDING PARTITIONS

PART 1 - GENERAL

1.01	RELATED DOCUMENTS

A.	Drawings and general provisions of Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

1.02	REFERENCES

A.	American Society of Testing and Materials (ASTM)

E 84	Test Method for Surface Burning Characteristics of Building Materials

E90	Test Method for Laboratory Measurement of Airborne Sound Transmission Loss of Building Partitions

E 413

E 557	Practice for Architectural Application and Installation of Operable Partitions

E 699

B.	Federal Specifications (FS)

CCC-W-408

1.03	SUMMARY

A.	This Section includes the following:

1.	Manually operated, pantographic assemblies.

1.04	SUBMITTALS

A.	General:  Submit the following in accordance with Conditions of Contract and Division 1 Specification Sections.

B.	Product data on physical characteristics, durability, resistance to fading, and flame resistance characteristics for each type of accordion folding partition and accessory specified.

C.	Shop drawings showing location and extent of accordion folding partitions.  Include plans, elevations, large-scale details of anchorages, and accessory items.  Indicate unit conditions at openings, typical and special details, and location and installation requirements for hardware and operators.  Indicate direction of travel and static and dynamic loading on the building structure.

D.	Samples for verification purposes of each type of material exposed to view.  Include samples of each facing material selected.

E.	Product certificates signed by manufacturers of accordion folding partitions certifying that their products comply with specified requirements.

F.	Acoustical Certification:  Submit  independent testing agency's certificate stating that product and materials furnished comply with specified requirements.  Include certified laboratory testing data indicating that materials and assembly meet specified test requirements and square-foot weight.

1.05	SYSTEM PERFORMANCE REQUIREMENTS

A.	Fire Performance Characteristics:  Provide accordion folding partitions with surface burning characteristics indicated below, as determined by testing assembled materials composed of surface coverings, backings, and other construction identical to those required in this section, per ASTM E 84, by a testing organization acceptable to authorities having jurisdiction.

1.	Flame Spread:  25 or less.

2.	Smoke Developed:  450 or less.

B.	Acoustical Performance:  Provide accordion folding partitions tested by independent testing laboratory acceptable to authorities having jurisdiction, for the following acoustic properties, according to the test method indicated:

1.	Sound Transmission Requirements:  Accordion folding partition assembly tested in a full-scale opening (14 feet by 9 feet) for laboratory sound transmission loss performance in accordance with ASTM E 90, determined by ASTM E 413 and rated for a STC plus or minus 1 as indicated:

a.	Sound Transmission Class (STC):  40.

1.06	QUALITY ASSURANCE

A.	Single-Source Responsibility:  Obtain accordion folding partitions and mounting hardware from one source from a single manufacturer.

B.	Testing Laboratory Qualifications:  To qualify for acceptance, an independent testing laboratory must demonstrate to Sandia Delegated Representative (SDR)'s satisfaction, based on evaluation of laboratory-submitted criteria conforming to ASTM E 699, that it has the experience and capability to conduct satisfactorily the testing indicated.

C.	All materials used shall not contain asbestos fibers or lead.

1.07	DELIVERY, STORAGE, AND HANDLING

A.	Deliver materials to project site in original factory wrappings and containers, clearly labeled with identification of manufacturer, brand name, quality or grade, fire performance characteristics, and lot number.

B.	Store only on edge, blocked off ground to prevent sagging and warping, in original undamaged packages and containers, inside well-ventilated area protected from weather, moisture, soiling, extreme temperatures, and humidity.

C.	Comply with instructions and recommendations of manufacturer for special delivery, storage, and handling requirements.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

Curtition

Foldoor/Holcomb and Hoke Mfg. Co.

Hufcor, Inc. (Hough Mfg. Corp.)

Modernfold, Inc.

Panelfold, Inc.

Won-Door Corp.

2.02	SUSPENSION SYSTEMS

A.	Carriers:  Four wheel at lead post and two wheel at intermediate spacing as required for size and weight of partition for ease of operation.

B.	Suspension Tracks:  Heavy-duty steel or aluminum, with overhead supports of adjustable steel hanger rods; heavy-duty, ball-bearing, trolley system supports specifically designed for use with size and type accordion folding partition assembly indicated.  Track deflection independent of structural support system no more than 1/360th of opening width.

1.	Track Option:  Prefinished ceiling contact guard or channel to protect finished ceiling surface from damage by moving door.

2.03	POSTS AND SEALS

A.	Lead posts and jamb post formed to provide rigidity for partition and light seal at adjacent construction.

B.	Seals:  Perimeter sweep strips for each side, top, and bottom, providing continuous contact with head and sill surfaces for positive light and sound seal.  Include manufacturer's standard male and female sound and light seal at lead post and jamb.

2.04	FINISH SURFACE

A.	Finish Surface:  Manufacturer's standard mildew resistant vinyl fabric complying with FS CCC-W-408A for Type 1 material and Class A fire rating.

B.	Materials:  Colors and patterns as selected by Sandia Delegated Representative (SDR) from manufacturer's standards.

2.05	HARDWARE

A.	Hardware:  Manufacturer's standard heavy-duty manually operated pulls and latches.

1.	Latches:  Operable from both sides of closed partitions.

2.	Pendant Pulls:  Near top of lead in addition to standard pull handle/latch for units over 10 feet high, 20 feet wide, or both.

PART 3 - EXECUTION

3.01	EXAMINATION

A.	Examine flooring for compliance with requirements for installation tolerances and other conditions affecting performance of accordion folding partitions.  Do not proceed with installation until unsatisfactory conditions have been corrected.

3.02	INSTALLATION

A.	Install accordion folding partitions and accessories in compliance with ASTM E 557 after other finishing, including painting, has been completed.

B.	Install folding partitions in conformance with drawings and approved shop drawings and in strict compliance with manufacturer's written installation instructions.

C.	Match accordion folding partitions for color and pattern by installing partitions from cartons in same sequence as manufactured and packaged, if so numbered.  Broken, cracked, chipped, or deformed partitions are not acceptable.

D.	Repair or replace accordion folding partitions within areas where test results indicate partitions do not comply with requirements and retest partitions.

3.03	ADJUSTING

A.	Lubricate bearings and sliding parts; adjust to ensure smooth, easy operation.

3.04	CLEANING

A.	Clean all accordion folding partition surfaces and clean adjacent surfaces.  Avoid use of abrasive cleaners or solutions containing corrosive solvents.  Use cleaning materials recommended by manufacturer.

END OF SECTION